NWOS2.DOC           07/10/91
          Copyright 1991, Compaq Computer Coprporation.
                                
   NOVELL NETWARE REQUESTOR FOR OS/2 INSTALLATION INSTRUCTIONS


CONTENTS

1. INTRODUCTION
2. SYSTEM REQUIREMENTS
3. INSTALLATION
4. NETWIRE


1. INTRODUCTION

     The device driver (CPQTOKNW.SYS) V1.04 allows a system using 
     MS OS/2 to attach to networks using Novell NetWare.  The
     following files are needed to support NetWare operation on
     OS/2:

          CPQTOKNW.SYS - OS/2 Device Driver
          OS2NET.CFG - Sample Configuration File

     In addition to these files, additional device drivers
     available from Novell are required to configure an MS OS/2
     system for use with Novell NetWare.  Refer to your Novell
     NetWare Requester for OS/2 documentation or contact an
     Authorized Novell NetWare Dealer for more information on the
     NetWare Requester for OS/2.


2. SYSTEM REQUIREMENTS

  This device driver requires:
     *    Any COMPAQ EISA computer with the COMPAQ 32-bit DualSpeed
          Token-Ring controller installed. The system must have
          been configured using the COMPAQ EISA Configuration
          Utility.
     
     *    MS OS/2 

     *    Novell NetWare Requester for OS/2


3. INSTALLATION

  In the following procedure, refer to your Novell NetWare
  OS/2 Requester documentation.

     1.   Follow the Novell OS/2 Requester installation
          instructions to copy device drivers and support files
          provided by Novell to your system.  Proceed to the step
          where you are instructed to edit the CONFIG.SYS file to
          choose the network interface board.

     2.   Instead of removing "rem" from the beginning of an
          existing network interface driver line, add the following
          line in the same section of the CONFIG.SYS file:
  
          DEVICE=C:\directory\CPQTOKNW.SYS
  
     NOTE:  Substitute for directory the name of the subdirectory
     into which you installed the other Novell NetWare Requester
     drivers in step 1.
  
     3.   Copy the CPQTOKNW.SYS file to the subdirectory you
          specified during the Novell Requester installation. 
          (This is the same subdirectory you added to the
          CONFIG.SYS file.)

     4.   You may create a section in the Novell Requester network
          configuration file, NET.CFG, to control several aspects
          of the CPQTOKNW.SYS driver operation.  These parameters
          and the NET.CFG file itself are completely optional.  The
          configuration options used in the NET.CFG file for the
          CPQTOKNW.SYS device driver are as follows:
  
          Frame frame_type    This keyword is generally required
                              when protocols other than IPX, such
                              as TCP/IP, are loaded. The variable
                              frame_type can be TOKEN-RING or
                              TOKEN-RING_SNAP.

          Node Address x      Overwrites the controller Burn-In  
                              Address.  The variable x must be 12
                              hexadecimal digits.  Default is the
                              Burn-In Address.
  
          No Earlyrelease     This keyword is for the token ring
                              controller running at 16 megabits per
                              second.  No parameters are necessary. 
                              The default is early token release
                              at 16 Mbps.
  
          Protocol IPX E0     This keyword specifies which protocol
                              is used with the driver. The example
                              above is Novell's IPX and its
                              protocol identification, defined by
                              Novell, is E0 (hex). This is also the
                              default for the driver.
  
          Source Routing      This keyword allows the MS OS/2
                              workstation to access a server that
                              is not on the same physical network
                              through source routing bridges.  No
                              parameters are necessary.  Default
                              is no source routing.
  
          Send Retries 3      This keyword configures the MLID to
                              attempt 3 retries on transmit
                              packets.  Default is 0 retries.
  
  Refer to the sample NET.CFG file and your Novell NetWare
documentation for more information on these and other parameters
that may be set in the NET.CFG file.


4. NETWIRE

     The NetWare OS/2 Requestor driver files for the COMPAQ 32-Bit
     DualSpeed Token Ring Controller reside on Compuserve NetWire
     under NOVA forum in library 11 (or library 17 for new uploads)
     in the CPQTR2.ZIP file.