POWER-QWK 2.14  August 1991  (c) Gale Green & Powerline Systems Ltd.

      This file, and the accompanying programs, form part of the POWER-QWK
      software package. They can ONLY be distributed as part of the
      complete POWER-QWK package. Power-Qwk is SHAREWARE.  Please register
      if you find the software of use.

      Ansi Art and Music
      ~~~~~~~~~~~~~~~~~~
      Introduction
      ~~~~~~~~~~~~
      From  release 2.06 onwards, Power-QWK supports  messages  containing
      Ansi  Music  as  well as the conventional  Ansi  colour  and  cursor
      movement  sequences and the Ansi Art files which were  supported  at
      release 2.05.

      This  document describes the Escape Sequences permitted by the  ANSI
      standard, as implemented by console drivers such as ANSI.SYS and its
      clones,  and highlights the differences between standard ANSI  files
      and Ansi Art and Music files.

      The  ANSI  standard defines Escape Sequences which may  be  embedded
      within Ascii text files to describe various characteristics of  that
      text  which are to be applied to it when it is displayed on a  video
      screen.

      The  'characteristics' describe such things as the colour  in  which
      the text is to be displayed, the position on the screen at which the
      text  is  to  be displayed, whether the  text  should  be  standard,
      intense or flashing, and so on.

      All  this information is read and used by the video driver  whenever
      the file is displayed.

      As  well  as  providing information to the VIDEO  driver  about  the
      formatting  of  subsequent  OUTPUT, the Escape  Sequences  may  also
      contain  instructions  which the video driver must pass  on  to  the
      KEYBOARD driver to tell it how it is to interpret subsequent  INPUT.
      A CONSOLE driver, like ANSI.SYS or one of its clones, embodies  both
      a  video  driver and a keyboard driver so such  information  is  not
      actually passed anywhere but is merely retained by ANSI.SYS when  in
      video mode for later use when in keyboard mode.

      An  Escape  Sequence is a series of characters which  always  starts
      with  the  character pair Esc[. That is, the  character  Escape,  or
      Ascii 27, followed by a left bracket.

      An Escape Sequence may be terminated by any one of the characters in
      the following list:

                 A, B, C, D, H, J, K, R, f, h, l, m, n, p, s, u

      Each  of  these  terminators defines a  particular  type  of  Escape
      Sequence,  thus  determining  the action to be taken  by  the  video
      driver  and  defining  what  other  characters  may  appear  in  the
      Sequence, between the Esc[ and the terminator.

      With  one exception, an Escape Sequence may not contain any  of  the
      terminator characters except as its last character.

      The exception, as we shall see later, is an Ansi Music Sequence.

      The next three sections describe the standard Ansi Escape Sequences,
      Ansi Art Escape Sequences and Ansi Music Escape Sequences.


      Standard Escape Sequences
      ~~~~~~~~~~~~~~~~~~~~~~~~~
      Esc[x;yH       These  each  move  the cursor to row x column y. Rows
      Esc[x;yf       are  numbered from 1 to 25; columns are numbered from
                     1 to  80. x and y each default to 1 if  omitted.

                     i.e., Esc[H  or  Esc[f  each move the cursor  to  the
                     Home position (top left hand corner of the screen);

      Esc[xA         Moves  the  cursor UP x rows (but not beyond  top  of
                     screen). Cursor column remains unchanged.

      Esc[xB         Moves  the cursor DOWN x rows (but not beyond  bottom
                     of screen). Cursor column remains unchanged.

      Esc[xC         Moves the cursor RIGHT x columns (but not beyond  the
                     right  hand edge of the screen). Cursor  row  remains
                     unchanged.

      Esc[xD         Moves  the cursor LEFT x columns (but not beyond  the
                     left  hand  edge of the screen). Cursor  row  remains
                     unchanged.

      Esc[s          Tells the video driver to remember the current cursor
                     position for later recall by Esc[u.

      Esc[u          Moves  the  cursor  to the last  position  stored  by
                     Esc[s.

      Esc[2J         Clears  the screen and moves the cursor to  the  Home
                     position (top left hand corner of the screen).

      Esc[K          Clears  the current row from cursor position  to  the
                     right hand edge of the screen.

      Esc[=xh        Set Screen to Mode x.

                          mode 0 -  40 by 25 black and white
                               1 -  40 by 25 colour
                               2 -  80 by 25 black and white
                               3 -  80 by 25 colour
                               4 -  320 by 200 colour
                               5 -  320 by 200 black and white
                               6 -  640 by 200 black and white
                               7 -  Set end-of-line wrap ON

      Esc[=xl        Reset screen to Mode x. (N.B., the 'l' is lower  case
                     L).

                     This is identical to 'Set Screen Mode', above, except
                     that when x is 7 end-of-line wrap is switched OFF.

      Esc[?7h        Set end-of-line wrap ON.

      Esc[.....m     Set Graphics Rendition

                     Between the Esc[ and the m may appear as many of  the
                     numbers in the following list as required,  separated
                     by  semi-colons. The numbers are  processed  strictly
                     left to right.

                      0 - reset  to system defaults of White  text,  Black
                          background,  High  Intensity (Bold)  OFF,  Blink
                          OFF.

                     The  remaining values only set particular  attributes
                     ON.

                     Therefore,  whenever you want to alter  Intensity  or
                     Blink,  you  are  obliged to reset  the  colours  you
                     require at the same time.

                      1 - Set High Intensity (Bold) ON.

                      5 - Set Blink ON.

                      8 - Set Conceal ON (renders the display invisible).

                     30 - Black   foreground ON
                     31 - Red     foreground ON
                     32 - Green   foreground ON
                     33 - Yellow  foreground ON
                     34 - Blue    foreground ON
                     35 - Magenta foreground ON
                     36 - Cyan    foreground ON
                     37 - White   foreground ON

                     40 - Black   background ON
                     41 - Red     background ON
                     42 - Green   background ON
                     43 - Yellow  background ON
                     44 - Blue    background ON
                     45 - Magenta background ON
                     46 - Cyan    background ON
                     47 - White   background ON

                     Examples:

                     Esc[45m        set  Magenta  background  leaving  all
                                    other attributes unchanged.

                     Esc[0;1;36m    set   Light   Cyan   text   on   Black
                                    background.

                     The following sequence displays the word 'Peacock' in
                     high  intensity flashing Blue on a  Cyan  background,
                     starting  at row 10 column 14. As an aid to  clarity,
                     the  character ` (leftward apostrophe) has been  used
                     to represent the Esc character.

                     `[0;1;5;34;46m`[10;14HPeacock

      Esc[....p      Keyboard  Reassignment (instructions to be passed  to
                     the keyboard driver).

                     Tells the keyboard driver that from now on, until the
                     machine is rebooted or another Reassignment  Sequence
                     is encountered, whenever the user types a  particular
                     character X, it is to be treated as though the string
                     Y had been typed.

                     X  may  be specified as a  single  character  between
                     quotes,  a single ASCII character code or  two  ASCII
                     codes (first one zero) separated by a semi-colon.

                     e.g.   the  character  z  (lower  case  Z)   may   be
                     represented as either "z" or 122 (the ASCII code  for
                     lower case Z).

                     The  F1  key is represented by the  two  ASCII  codes
                     0;59.

                     Most  of  the  available ASCII  character  codes  are
                     listed at the end of this document.

                     The entire string between Esc[ and p is treated as an
                     extended  ASCII  string. The first one or  two  codes
                     define   the  character  being  reassigned  and   the
                     remainder  define  the value to be assigned  to  that
                     character  whenever its corresponding key is  pressed
                     on the keyboard.

                     Remember,  these  codes must be OUTPUT in  order  for
                     them  to  be interpreted and passed to  the  keyboard
                     driver to affect INPUT.

                     Therefore, to use any of the keyboard  reassignments,
                     you  must place the necessary Escape Sequences  in  a
                     file  and  then display the file using the  DOS  TYPE
                     command (and a driver like ANSI.SYS must be loaded at
                     the time).

                     Examples:

                     Esc[0;59;"dir/w";13p     causes  dir/w<Return> to  be
                                              typed whenever you press F1

                     Esc["xy"p      causes  y  to be  typed  whenever  you
                                    press x.

                     Esc[120;121p   causes  y  to be  typed  whenever  you
                                    press x.

                     Esc[120;120p   resets character 120 (lower case x) to
                                    its normal state.

                     Esc[0;25;"PQ";13p   causes  PQ<Return>  to  be  typed
                                         whenever you press Alt/p.

      The  keyboard reassignment sequences are potentially very  dangerous
      because they can be embedded within files to cause 'secret'  changes
      to  the keyboard assignments whenever the file is displayed  with  a
      console driver in residence.

      This is how certain Trojan viruses work.

      Various  mechanisms  have been adopted to avoid  such  viruses.  For
      instance,  Power-QWK has its own in-built ANSI driver which  totally
      ignores all keyboard reassignments within files and messages.

      A  further  precautionary measure has been taken to  avoid  problems
      with Ansi Art, as we shall see...

      Ansi Art Escape Sequences
      ~~~~~~~~~~~~~~~~~~~~~~~~~

      These  are  exactly  as described above  for  Standard  ANSI  Escape
      Sequences  except that the Esc character (Ascii 27) is  replaced  by
      one of the characters Ascii 249 (ù) Ascii 250 (ú) or Ascii 96 (`).

      The  reason for this change is that it prevents the introduction  of
      Trojan viruses via Ansi keyboard reassignment sequences, if the file
      is  ever displayed using a keyboard driver like ANSI.SYS or  any  of
      its clones.

      Power-QWK automatically ignores keyboard reassignment sequences when
      displaying received files and messages but this may not be the  case
      with more primitive implementations of the ANSI standard.


      Ansi Music Escape Sequences
      ~~~~~~~~~~~~~~~~~~~~~~~~~~~

      Ansi  Music  files  and messages may contain all  of  the  Sequences
      described above for Standard Ansi files, but with the Esc  character
      changed to Ascii 250 or Ascii 96, as described for Ansi Art files.

      They may also contain Music Escape Sequences in the following format
      (remember that the notation Esc, here, means Ascii 250 or Ascii 96).

               Esc[............<Ascii 14>

      i.e.,     Esc[   as  usual,  then  a  series  of  musical   commands
                terminated by the character Ascii 14.


      Ascii  14  is  the  character  'double quaver'  (or  is  it  'double
      crotchet'),  it's a musical note in any case. Many editors  and word
      processors  do  not  allow  the  use of this character. See the next
      section  'Placing ANSI Sequences into Files and Messages'.

      If the program being used to read this document allows the character
      Ascii 14 then you will see one here: 


      The  musical  commands  are exactly as used  by  the  GW-BASIC  PLAY
      command.  There  are  a total of 85 different  notes  where  note  0
      represents silence and notes 1 through 84 are audible.

      These  notes  between them cover seven octaves, numbered  0  (deeper
      notes) to 6 (higher notes).

      The musical commands are obeyed strictly left to right.

      The commands available are as follows:

       On       change to Octave n (n range 0 through 6)

       >        if current octave is less than 6 then increase it by 1.

       <        if current octave is greater than 0 then decrease it by 1.

       Nn       play note n (n range 0 to 84 where 0 = rest)

                See note table at the end of this document.

       Ln       set duration for subsequent notes.

                1 = whole note; 2 = half note; 4 = quarter note and so on.

       Pn       pause for duration n. n is as described for Ln.

       A..G     play  the note specified (A to G). May be followed by  '#'
                or '+', indicating 'sharp' or '-', indicating 'flat'.

                Examples:  A F B# C- D+

                To  set a duration for just the current note,  over-riding
                any  duration previously set using Ln, write the  duration
                after the note.

                e.g., L4 A B#2 C

                plays  quarter-length A, followed by half-length B  sharp,
                followed by quarter-length C.

                One  or more dots (.) following a note each indicate  that
                the  previously computed duration is to be  multiplied  by
                1.5

       Tn       set the tempo for subsequent notes. n specifies the number
                of  L4's (quarter notes) that there are in one  minute.  n
                must lie in the range 32 to 255. It defaults to 120.

       MN       set  'Music Normal'. Subsequent notes will play for  seven
                eighths of their computed duration.

                This is the default used by Power-QWK if none of MN, ML
                or MS has been specified.

       ML       set  'Music  Legato'. Subsequent notes will play  for  the
                whole of their computed duration.

       MS       set 'Music Staccato'. Subsequent notes will play for three
                quarters of their computed duration.

       MF       set  'Music Foreground'. Stop all other  processing  until
                music has finished.

       MB       set  'Music Background'. Continue other  processing  while
                music plays.

                At  least  initially,  this  mode  is  not  supported   by
                Power-QWK. Ansi Music strings may contain MB commands but
                Power-QWK treats them as MF.

      Some  mail  programs  insist  that  music  sequences  begin with the
      sequence MB. That is to say, music sequences must have  the  general
      form

             Esc[MB.........<Ascii 14>

      Power-QWK is not so fussy - the Esc[ may be followed immediately  by
      any 'M' command - MB, MF, ML, MN or MS.

      This increases Power-QWK's tolerance of common errors.

      For the  same  reason,  Power-QWK  permits  music  sequences  to  be
      terminated by end-of-line as well as the more usual Ascii 14.

      When reading Ansi messages with Power-QWK, you will find  that  more
      received music will actually play than with ordinary  mail  readers,
      simply because Power-QWK is more forgiving of composer errors.

      Placing Ansi Escape Sequences into Files and Messages
      ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

      There are three main areas of difficulty:

            1.  Changing Esc characters to Ascii 249, 250 or 96.

                If  you  do  not have an editor  which  supports  the  Esc
                character,  then  use the utility  ansi2art.exe,  supplied
                with Power-QWK. Just type

                ansi2art <filename>

                You  will be asked whether to replace Esc characters  with
                Ascii  249, 250 or 96  (Power-QWK doesn't mind  which  you
                use).  If  you use one and find that your  online  service
                doesn't like it, change to the other.

                To change a file back to ordinary Esc characters, type

                art2ansi <filename>

                These  utilities are also useful for converting  Ansi  Art
                pictures, as output by programs such as TheDraw.

                If you ask TheDraw to file your picture in Ansi format, it
                will  produce  a  'real' Ansi file where  all  the  Escape
                Sequences start with 'real' Escape characters.

                This file can be converted to Ansi Art format by typing

                ansi2art <filename>


            2.  Adding Ascii 14 to the ends of Ansi Music Sequences.

                If your editor or word processor doesn't support Ascii  14
                then use EDLIN.

                To  enter Ascii 14 when using EDLIN, type Ctrl/V  followed
                by  the character N. The notation Ctrl/V means 'hold  down
                the  Ctrl key; press the V key once and then release  both
                keys'.

                Pressing  Ctrl/Vx (x any character) tells EDLIN that  what
                you really want is Ctrl/x.

                Ctrl/N is Ascii 14.

                If you are sending a private message to another  Power-QWK
                user  then  you may find it useful that Power-QWK,  as  an
                extension  to the standard, allows you to  terminate  Ansi
                Music sequences with the ] character as well as with Ascii
                14  (because  any  editor will allow you  to  type  the  ]
                character).

                Thus, Power-QWK Music sequences can take the form

                         Esc[Mx..............]

                Where Esc can be Ascii 27, 249, 250 or 96 and x may be any
                of the characters which are allowed to follow M - F, B, N,
                L or S.

                But  remember this is a Power-QWK convention.  Other  mail
                readers will not recognise any terminator but Ascii 14 and
                may expect the first music command to be MB.

            3.  Entering Esc characters

                To  enter 'ordinary' Escape characters into a file,  again
                use EDLIN if your editor or word processor won't oblige.

                Remember  that  Escape  is  just  another  name  for   the
                character Ctrl/[.

                Therefore, to enter an Escape character in EDLIN, type

                Ctrl/V[

                To enter the sequence Esc[0;25;"PQ";13p type

                Ctrl/V[[0;25;"PQ";13p

                (Note that there are two [ characters - one combines  with
                Ctrl/V to form an Escape character, the other is just a  [
                character).

      The Ansi Music Note Table
      ~~~~~~~~~~~~~~~~~~~~~~~~~
      The  number  suffix on each note below indicates octave.  e.g.,  the
      notation D#5 indicates the note D sharp in octave 5.

                No.  Note Frequency      No.  Note Frequency
                ~~~  ~~~~ ~~~~~~~~~      ~~~  ~~~~ ~~~~~~~~~

                 1   C1   65             43   F#4  740
                 2   C#1  69             44   G4   784
                 3   D1   73             45   G#4  831
                 4   D#1  78             46   A4   880
                 5   E1   82             47   A#4  932
                 6   F1   87             48   B4   988
                 7   F#1  93             49   C5   1047
                 8   G1   98             50   C#5  1109
                 9   G#1  104            51   D5   1175
                10   A1   110            52   D#5  1245
                11   A#1  116            53   E5   1319
                12   B1   123            54   F5   1397
                13   C2   131            55   F#5  1480
                14   C#2  139            56   G5   1568
                15   D2   147            57   G#5  1661
                16   D#2  156            58   A5   1760
                17   E2   165            59   A#5  1865
                18   F2   175            60   B5   1976
                19   F#2  185            61   D#7  2093
                20   G2   196            62   E7   2217
                21   G#2  208            63   F7   2349
                22   A2   220            64   C6   2489
                23   A#2  233            65   C#6  2637
                24   B2   247            66   D6   2794
                25   C3   262            67   D#6  2960
                26   C#3  277            68   E6   3136
                27   D3   294            69   F6   3322
                28   D#3  311            70   F#6  3520
                29   E3   330            71   G6   3729
                30   F3   349            72   G#6  3951
                31   F#3  370            73   A6   4186
                32   G3   392            74   A#6  4435
                33   G#3  415            75   B6   4699
                34   A3   440            76   C7   4978
                35   A#3  466            77   C#7  5274
                36   B3   494            78   D7   5587
                37   C4   523            79   F#7  5919
                38   C#4  554            80   G7   6271
                39   D4   587            81   G#7  6645
                40   D#4  622            82   A7   7040
                41   E4   659            83   A#7  7459
                42   F4   698            84   B7   7902

      Ascii Character Codes
      ~~~~~~~~~~~~~~~~~~~~~
                       INPUT Characters

                         Alone  Shift  Ctrl   Alt

           1.............49     33     -      0;120
           2.............50     64     -      0;121
           3.............51     35     -      0;122
           4.............52     36     -      0;123
           5.............53     37     -      0;124
           6.............54     94     -      0;125
           7.............55     38     -      0;126
           8.............56     42     -      0;127
           9.............57     40     -      0;128
           0.............48     41     -      0;129

           A.............97     65     1      0;30
           B.............98     66     2      0;48
           C.............99     67     3      0;46
           D.............100    68     4      0;32
           E.............101    69     5      0;18
           F.............102    70     6      0;33
           G.............103    71     7      0;34
           H.............104    72     8      0;35
           I.............105    73     9      0;23
           J.............106    74     10     0;36
           K.............107    75     11     0;37
           L.............108    76     12     0;38
           M.............109    77     13     0;50
           N.............110    78     14     0;49
           O.............111    79     15     0;24
           P.............112    80     16     0;25
           Q.............113    81     17     0;16
           R.............114    82     18     0;19
           S.............115    83     19     0;31
           T.............116    84     20     0;20
           U.............117    85     21     0;22
           V.............118    86     22     0;47
           W.............119    87     23     0;17
           X.............120    88     24     0;45
           Y.............121    89     25     0;21
           Z.............122    90     26     0;44

           F1............0;59   0;84   0;94   0;104
           F2............0;60   0;85   0;95   0;105
           F3............0;61   0;86   0;96   0;106
           F4............0;62   0;87   0;97   0;107
           F5............0;63   0;88   0;98   0;108
           F6............0;64   0;89   0;99   0;109
           F7............0;65   0;90   0;100  0;110
           F8............0;66   0;91   0;101  0;111
           F9............0;67   0;92   0;102  0;112
           F10...........0;68   0;93   0;103  0;113



                         Alone  Shift  Ctrl   Alt

           Insert........0;82   48     -      -
           Delete........0;83   46     -      -

           Home..........0;71   55     0;119  -
           End...........0;79   49     0;117  -

           PgUp..........0;73   57     0;132  -
           PgDn..........0;81   51     0;118  -

           Cursor Up.....0;72   56     -      -
           Cursor Down...0;80   50     -      -
           Cursor Left...0;75   52     0;115  -
           Cursor Right..0;77   54     0;116  -

           Print Screen..-      -      0;114  -
           Tab...........9      0;15   -      -
           Return........13     -      -      -

           -.............45     95     -      0;130
           =.............61     43     -      0;131


               The Extended ASCII INPUT Character Set


      Sorry about the numbering in this section - I'll change it one day.

      This table I originally used in a different document where this
      sequence made sense!



        1. ^A             32. space           63. ?               94. ^

        2. ^B             33. !               64. @               95. _

        3. ^C (Break)     34. "               65. A               96. `

        4. ^D             35. #               66. B               97. a

        5. ^E             36. $               67. C               98. b

        6. ^F             37. %               68. D               99. c

        7. ^G (Bell)      38. &               69. E              100. d

        8. ^H (Backspace) 39. '               70. F              101. e

        9. ^I (Tab)       40. (               71. G              102. f

       10. ^J (Linefeed)  41. )               72. H              103. g

       11. ^K             42. *               73. I              104. h

       12. ^L             43. +               74. J              105. i

       13. ^M (Return)    44. ,               75. K              106. j

       14. ^N             45. -               76. L              107. k

       15. ^O             46. .               77. M              108. l

       16. ^P             47. /               78. N              109. m

       17. ^Q             48. 0 (zero)        79. O              110. n

       18. ^R             49. 1               80. P              111. o

       19. ^S             50. 2               81. Q              112. p

       20. ^T             51. 3               82. R              113. q

       21. ^U             52. 4               83. S              114. r

       22. ^V             53. 5               84. T              115. s

       23. ^W             54. 6               85. U              116. t

       24. ^X             55. 7               86. V              117. u

       25. ^Y             56. 8               87. W              118. v

       26. ^Z             57. 9               88. X              119. w

       27. Escape (^[)    58. :               89. Y              120. x

       28. ^\             59. ;               90. Z              121. y

       29. ^]             60. <               91. [              122. z

       30. ^^             61. =               92. \              123. {

       31. ^- or ^_       62. >               93. ]              124. |


      Next page...

      125. }             158. ž (ª3)         191. ¿              224. à

      126. ~             159. Ÿ              192. À              225. á

      127. ^backspace    160.                193. Á              226. â

      128. €             161. ¡              194. Â              227. ã

      129. �             162. ¢              195. Ã              228. ä

      130. ‚             163. £              196. Ä              229. å

      131. ƒ             164. ¤              197. Å              230. æ

      132. „             165. ¥              198. Æ              231. ç

      133. …             166. ¦              199. Ç              232. è

      134. †             167. §              200. È              233. é

      135. ‡             168. ¨              201. É              234. ê

      136. ˆ             169. ©              202. Ê              235. ë

      137. ‰             170. ª              203. Ë              236. ì

      138. Š             171. «              204. Ì              237. í

      139. ‹             172. ¬              205. Í              238. î

      140. Œ             173. ­              206. Î              239. ï

      141. �             174. ®              207. Ï              240. ð

      142. Ž             175. ¯              208. Ð              241. ñ

      143. �             176. °              209. Ñ              242. ò

      144. �             177. ±              210. Ò              243. ó

      145. ‘             178. ²              211. Ó              244. ô

      146. ’             179. ³              212. Ô              245. õ

      147. “             180. ´              213. Õ              246. ö

      148. ”             181. µ              214. Ö              247. ÷

      149. •             182. ¶              215. ×              248. ø

      150. –             183. ·              216. Ø              249. ù

      151. —             184. ¸              217. Ù              250. ú

      152. ˜             185. ¹              218. Ú              251. û

      153. ™             186. º              219. Û              252. ü

      154. š             187. »              220. Ü              253. ý

      155. ›             188. ¼              221. Ý              254. þ

      156. œ             189. ½              222. Þ              255. Spce

      157. �             190. ¾              223. ß

This file, and the accompanying programs and Doc files are (c) Gale Green &
                     Powerline Systems Ltd.  June 1991