Shareware Documentation            QB/EVGFX (C)1990 Cornel Huth
with minor changes 21-Mar-92 chh

Complete documentation is available with registration.  See the
end of this document for complete ordering information.

Shareware, def.  A try-before-you-buy marketing concept.  It
relies on those that benefit from the product to pay for it.  Go
ahead and try before you buy.  If you can't use it, pass it
along, someone else may.  If you can and do use it, pay for it. 
What do you get for your money?  Not only the legal continued use
of the product but you also get personal support from the author. 
Need something changed for a particular need?  Just ask.  Try
that anywhere else.  Just remember, this product is not free, so
if you use it please pay for it.


OVERVIEW

QB/EVGFX is a set of graphic routines for the EGA and VGA
assembled into a linkable LIB file.  All routines have been
written in 8086 assembly and are self-contained.  In other words,
even though QB/EVGFX has been designed for QuickBASIC 4.00+
compilers, QuickBASIC itself is not needed.

QB/EVGFX requires an EGA or VGA compatible video card with at
least 256K of RAM.  It can be used in any native EGA and VGA mode
and also extended modes.  All these routines will work on either
an EGA or VGA.

Accept the fact that these routines are for programmers. 
Understand that this documentation is for programmers.
If you are not completely familiar with QB, BC, LINK and LIB, do
not fault this documentation.  Consult the appropriate reference
or register this release to receive the 70-plus-page programmer
reference manual.  The manual describes each routine completely
and offers ideas on how it, and QB/EVGFX, can best be used.

@@@@@@@@ Version 1.1 is the latest and greatest release of QB/EVGFX @@@@@@@@@@@
@                                                                             @
@ This shareware release you now have is 1.0, the original. Release 1.1       @
@ has a few more routines (like dithered windows), cleaned-up docs, better    @
@ window parameters (x/y-size rather than end-points), more fonts (70+),      @
@ pixel-precision windowed draw routines, and more I can't remember now.      @
@ Release 1.0 was distributed through limited channels nearly 1 1/2 years     @
@ ago. This re-release through PDN (thanks Erik! et. al) should result in a   @
@ greater exposure and that's what shareware is all about. -- Granted, these  @
@ docs in this shareware release won't make you an instant expert, but it sure@
@ should give you a good idea of what this package can do for you. To order   @
@ your copy see the form at the end of this documentation and in !ORDER.FRM.  @
@                                                                             @
@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@@

----------------------------------------------------------------
* Some routines require a variable-length string in DGROUP as a 
* parameter.  If you don't have this capability, see the section
* on simulating this data structure.
----------------------------------------------------------------


-----------------------
QB/EVGFX COMMAND SUMMARY
 VIDEO CONTROL ROUTINES
 DRAWING ROUTINES
 FONTS
 MISC ROUTINES

-------------------------------
VIDEO CONTROL ROUTINES include:

EGAVIDEO,VGAVIDEO,COLORVIDEO
SETMODE,SETMODEX,GETMODE
SETPSA,GETPSA
SETPALREG,SETPALETTE
SETSCNBUFF
BLANKSCN
BLINKBIT
WAITVS


FUNCTION EGAVIDEO%()
EGAVIDEO returns -1 if EGA video is supported, 0 if not.
Eg>IsEGA = EGAVIDEO


FUNCTION VGAVIDEO%()
VGAVIDEO returns -1 if VGA video is supported, 0 if not.
Eg>IsVGA = VGAVIDEO


FUNCTION COLORVIDEO%()
COLORVIDEO returns -1 if color video is supported, 0 if not.
Eg>IsColor = COLORVIDEO


SUB SETMODE(mode%)
SETMODE sets the computer's BIOS video to mode.  
Normal EGA 640x350x16 graphics (QB SCREEN 9) is SETMODE 16.
Normal VGA 640x480x16 graphics (QB SCREEN 12) is SETMODE 18.
Eg>SETMODE &H10


SUB SETMODEX(regax%,regbx%)
SETMODEX is similar to SETMODEX but allows setting the computer's
BIOS mode to an extended mode.  Most extended modes require only
the AL register, in which case SETMODE can be used.  However,
some video adapter's extended modes need an additional register
to also be set (eg EVEREX).  Consult your adapter manual.
Eg>SETMODEX &H0070,&H0


FUNCTION GETMODE%()
GETMODE returns the current BIOS video mode.
Eg>VMode = GETMODE


SUB SETPSA(onoff%)
SETPSA activates/deactivates the palette save area. 
SETPSA 1 activates the BIOS palette save area.  Any future
changes in the palette will be stored there for later recall.
SETPSA 0 deactivates the BIOS palette save area.  If you activate
the PSA in your program you MUST deactivate it before the program
ends.
Eg>SETPSA 1


SUB GETPSA(pal17$)
GETPSA returns a table of palette values and border color.  The
variable pal17$ is a variable length string in DGROUP. The first
byte of pal17$ returned is the color value for attribute 0,
second byte is attribute 1, and so on.  Byte 17 of pal17$ is the
color border value.  This routine should only be used if there is
an active palette save area (SETPSA 1).
Eg>GETPSA pal17$


SUB SETPALREG(reg%,colorval%)
SETPALREG sets one of the palette registers.  Attribute 0 is
controlled by register 0, attribute 1 by register 1...up to
register 17 which is the border color.  Colorval is any color
value between 0 and 63.
Eg>SETPALREG 8,&H37


SUB SETPALETTE(pal17$)
SETPALETTE sets all 16 palette registers and the border with a
single call.  The variable pal17$ is a variable length string in
DGROUP.  The first byte of pal17$ is the color value for
attribute 0, second byte is attribute 1, and so on.  Byte 17 of
pal17$ is the border color value.  
Eg>SETPALETTE pal17$


SETSCNBUFF(x1%,y1%)
SETSCNBUFF set the logical dimensions of the video display
buffer.  This should be done after every video mode change. 
Standard dimensions are x1%=640, y1%=350 for EGA mode 16,
x1%=640,y1%=480 for VGA mode 18.
Eg>SETMODE &H12
Eg>SETSCNBUFF 640,480


BLANKSCN(onoff%)
BLANKSCN turns the video system on or off.
BLANKSCN 1 turns the video off.
BLANKSCN 0 turns the video back on.
Eg>BLANKSCN 1


BLINKBIT(onoff%)
BLINKBIT allows selecting either 16 possible background values or
8 background values and 8 blinking.  The palette needs to be
adjusted on the EGA before using BLINKBIT 1.
Eg>BLINKBIT 1


WAITVS(count%)
WAITVS waits for count% vertical sync signals.  In EGA mode 16
and VGA mode 18 a vert sync is at least 1/60th of a second. 
Eg>WAITVS 1


-------------------------
DRAWING ROUTINES include:

READDOT,DRAWDOT
DRAWCH
SETSTEP,GETSTEP
DRAWLN,DRAWLNP,DRAWLNS
DRAWSTR
DRAWELL
FILLSCN,FILLAREA,FILLAREAP,FLUDAREA,FLUDAREAP
DIMBLOCK,GETBLOCK,PUTBLOCK


The x and y coordinates are screen coordinates with 0,0 at the
upper-left of the screen.  x runs across, y runs down.

The value is an attribute value, 0 to 15.  Eg, using a value of 7
would use the color value in attribute register 7.

The mode is the method used when updating the pixels.  A mode=0
replaces the pixels, mode=8 ANDs the pixels, mode=16 ORs the
pixels, and mode=24 XORs the pixels.


FUNCTION READDOT%(x0%,y0%)
READDOT returns the value of the pixel at position x0,y0.
Eg>dot = READDOT(320,175)


SUB DRAWDOT(mode%,value%,x0%,y0%)
DRAWDOT sets the pixel by mode at position x0,y0 to value.
Eg>DRAWDOT 0,7,320,175


SUB DRAWCH(mode%,char%,x0%,y0%,fg%,bg%)
DRAWCH draws ASCII char by mode at position x0,y0 in foreground
value fg, background bg.
Eg>DRAWCH 0,65,0,0,7,0


SUB DRAWLN(mode%,value%,x0%,y0%,x1%,y1%)
DRAWLN draws a line by mode from x0,y0 to x1,y1 in value.
Eg>DRAWLN 0,7,0,0,639,349


SUB DRAWLNP(mode%,pattern$,x0%,y0%,x1%,y1%)
DRAWLNP draws a line by mode from x0,y0 to x1,y1 using the
pattern pattern$.  The first byte of pattern$ is to be the shift
count, the other bytes are the attribute values to use as the
pattern.  Though not all that useful in DRAWLNP, the shift count
lets you fill with diagonal patterns in the pattern fill
routines. 
Eg>pattern$=chr$(0)  'no shift after each line
Eg>for i=1 to 15:pattern$ = pattern$ + chr$(i):next
Eg>DRAWLNP 0,pattern$,0,0,320,175


SUB SETSTEP(x0%,y0%)
SETSTEP sets the x0,y0 point for DRAWLNS.
Eg>SETSTEP 320,175


SUB GETSTEP(x0%,y0%)
GETSTEP returns the current x0%,y0% step point.
Eg>GETSTEP x0,y0
Eg>PRINT x0;y0   'x0=320,y0=175


SUB DRAWLNS(mode%,value%,x1%,y1%)
DRAWLNS draws a line by mode from step point to x1,y1 in value. 
The initial step point is set using SETSTEP, thereafter, DRAWLNS
updates the step point.  You cannot have any other QB/EVGFX
routines between successive DRAWLNSs.
Eg>DRAWLNS 0,7,310,160


FUNCTION DRAWSTR%(mode%,strg$,x0%,y0%,fg%,bg%,gap%)
DRAWSTR draws a text string by mode starting at x0,y0 in
foreground value fg, background bg, with an inter-character gap
of gap.  If gap=0 the inter-character gap is taken from the
font's width table for proportional spacing.  DRAWSTR returns the
next available x-position after the end of the string.
Eg>nx=DRAWSTR(0,"Drawn in proportional space...",0,0,7,0,0)


SUB DRAWELL(mode%,value%,xC%,yC%,maj%,min%)
DRAWELL draws an ellipse by mode with the center at xC,yC with an
x-radius of maj, y-radius of min, in value.
Eg>DRAWELL 0,7,320,175,100,130


SUB FILLSCN(lines%,value%)
FILLSCN fills the screen buffer starting at 0,0 for lines count,
in value.
Eg>FILLSCN 350,0


SUB FILLAREA(mode%,newval%,borderval%,x%,y%)
FILLAREA will boundary-fill any shape by mode, bounded by
borderval completely enclosing x,y, with newval.  For each level
of complexity, FILLAREA uses 12 bytes of stack space.  Many areas
can be filled with as little at 12 bytes (an empty circle) while
others can require more, perhaps 1K (very complex).  In any case,
by changing the DECLARE of FILLAREA from a SUB to a FUNCTION, you
can get the maximum number of bytes used on the stack, say, for
debugging purposes.
Eg>DECLARE FILLAREA%(mode%,newval%,borderval%,x%,y%)
Eg>maxbytes=FILLAREA(0,5,7,320,175)


SUB FILLAREAP(mode%,pattern$,borderval%,x%,y%)
FILLAREAP will boundary-fill any non-complex shape by mode,
bounded by borderval completely enclosing x,y, with pattern$. 
FILLAREAP cannot make complex pattern fills.  For complex pattern
fills, use FLUDAREAP.  See DRAWLNP for the structure of pattern$.
Eg>FILLAREAP 0,pattern$,7,320,175)


SUB FLUDAREA(mode%,newval%,x%,y%)
FLUDAREA will flood-fill any shape by mode that has the value at
x,y, with newval.  The difference between FLUDAREA and FILLAREA
is that FILLAREA stops when it reaches a borderval, going over
any other value.  FLUDAREA stops when it reaches any value other
than the value at the seed, x,y.  For stack usage, see FILLAREA.
Eg>FLUDAREA 0,15,320,175


SUB FLUDAREAP(mode%,pattern$,x%,y%)
FLUDAREAP will flood-fill any shape by mode that has the value at
x,y, with pattern$.  For stack usage, see FILLAREA.  See DRAWLNP
for the structure of pattern$.
Eg>FLUDAREAP 0,pattern$,320,175


FUNCTION DIMBLOCK&(pmask%,x0%,y0%,x1%,y1%)
DIMBLOCK is used to calculate the number of bytes needed to store
the block defined by the upper-left coordinates x0,y0 and lower-
right coordinates x1,y1, based on the plane mask, pmask.  Pmask
is the mask value of planes to be used where 0 is no planes and
15 is all 4 planes (pmask=3 uses planes 0 & 1...).
Eg>sz& = DIMBLOCK&(15,0,0,79,99)
Eg>PRINT sz&   'size = 4006 bytes


SUB GETBLOCK(pmask%,x0%,y0%,x1%,y1%,vseg%,voff%)
GETBLOCK stores to RAM the block defined by the upper-left
coordinates x0,y0 and the lower-right coordinates x1,y1, based on
the plane mask, pmask.  The vseg and voff parameters are the
VARSEG and VARPTR to the storage area in RAM.
Eg>REDIM buff(0 TO sz&) AS STRING * 1
Eg>GETBLOCK 15,0,0,79,99,VARSEG(buff(0)),VARPTR(buff(0))


SUB PUTBLOCK(mode%,x0%,y0%,vseg%,voff%)
PUTBLOCK stores to the video buffer by mode the block in RAM to
the upper-left coordinates x0,y0.  The block in RAM is pointed to
by the vseg and voff parameters.
Eg>PUTBLOCK 0,1,1,VARSEG(buff(0)),VARPTR(buff(0))


----------------------
FONT ROUTINES include:

FONTSYS08,FONTSYS14,FONTSYS16,FONTSRF14P
USERFONT


SUB FONTSYS08()
FONTSYS08 makes the DRAWCH and DRAWSTR routines use the system
8x8 font in adapter ROM.
Eg>FONTSYS08


SUB FONTSYS14()
FONTSYS14 makes the DRAWCH and DRAWSTR routines use the system
8x14 font in adapter ROM.
Eg>FONTSYS14


SUB FONTSYS16()
FONTSYS16 makes the DRAWCH and DRAWSTR routines use the system
8x16 font in adapter ROM.  This is a VGA-only font.  On EGA
systems this call will use the 8x14 font.
Eg>FONTSYS16


SUB FONTSRF14P()
FONTSRF14P is the proportional font included in the shareware
release of QB/EVGFX.  Many other fonts and a font editor are
available.  With them the programmer can create callable or user
fonts. 
Eg>FONTSRF14P


SUB USERFONT(vseg%,voff%,pts%)
USERFONT defines a dynamic font.  By using this routine, the
programmer can use fonts stored on disk rather than having all
fonts linked in memory.  Vseg and voff point to the font data,
pts is the height of the font.  The programmer allocates storage
for the largest font to be used, then loads the font data from
disk into the storage area.  The area can be reused.
Eg>REDIM buff(0 TO 8448) AS STRING * 1 'max 32 pts+width table
Eg>DoLOADUF font$,buff()
Eg>USERFONT VARSEG(buff(0)),VARPTR(buff(0)),pts


----------------------
MISC ROUTINES include:

GETBIT,SETBIT,XORBIT


FUNCTION GETBIT%(BYVAL CheckMe%,BYVAL BitPos%)
GETBIT returns non-zero if the bit at BitPos is set in CheckMe. 
BitPos is 15-0 with bit 15 the most significant, 0 the least.
Eg>set = GETBIT(CheckMe,15)


FUNCTION SETBIT%(BYVAL UseMe%,BYVAL BitPos%)
SETBIT sets the bit at BitPos returning the new value.
Eg>UseMe = SETBIT(UseMe,0)


FUNCTION XORBIT%(BYVAL XorMe%,BYVAL BitPos%)
XORBIT toggles the bit at BitPos returning the new value.
Eg>NewXorMe = XORBIT(XorMe,15)



-------------------------------------------------
In addition to the shareware release of QB/EVGFX:
QB/EVGFX2, QB/EVGFX plus window and 2-D routines:

SUB SETWIN2D(vseg2%,voff2%)
SETWIN2D defines the 2-D window.

SUB GETWIN2D(vseg2%,voff2%)
GETWIN2D returns the window definitions.

SUB SETSCNORG(x0%,y0%)
SETSCNORG positions the hardware display start address allowing
smooth-scrolling of the video buffer, page flipping...

FUNCTION DRAWSTRW%(mode%,strg$,x0%,y0%,fg%,bg%,gap%)
DRAWSTRW is identical to DRAWSTR except it only draws characters
that are within the defined window.

SUB DRAWELLW(mode%,value%,xC%,yC%,maj%,min%)
DRAWELLW is identical to DRAWELL except that it draws only within
the defined window.  DRAWELLW can also be used to draw arcs.

SUB FILLWIN(mode%,value%)
FILLWIN fills the defined window with value.

SUB FILLWINP(mode%,pattern$)
FILLWINP fills the defined window with pattern$.

SUB XFORM2D(vseg2%,voff2%)
XFORM2D performs complete transformations in 2-D on any number of
2-D points.  Rotation degrees, rotational center, x-axis
translation, y-axis translation, x-axis scale, y-axis scale, can
all be done with a single call.

FUNCTION CLIP2D%(vsegln2%,voffln2%)
CLIP2D performs the classic Sutherland-Cohen algorithm to clip
lines to the defined window.  Approximately 1000 lines per second
per MHz CPU speed can be clipped (33000 lines/sec on a 386/33).



------------------------------------------------------------
In addition to the shareware release QB/EVGFX and QB/EVGFX2:
QB/EVGFX3, QB/EVGFX plus QB/EVGFX2 plus 3-D routines:

SUB SETWIN3D(vseg3%,voff3%)
SETWIN3D defines the 3-D window.

SUB GETWIN3D(vseg3%,voff3%)
GETWIN3D returns the window definitions.

SUB XFORM3D(vseg3%,voff3%)
XFORM3D performs complete transformations in 3-D on any number of
3-D points.  Rotation heading, pitch, bank, rotational center, x-
 & y- & z-axis translation, x- & y- & z-axis scale can all be
done with a single call.

FUNCTION CLIP3D%(vsegln3%,voffln3%)
CLIP3D performs the classic Sutherland-Cohen algorithm to clip
lines to the defined window.  Approximately 1000 lines per second
per MHz CPU speed can be clipped (33000 lines/sec on a 386/33).

SUB PROJORTHO(vseg3%,voff3%)
PROJORTHO performs orthographic parallel projection conversion on
a set of 3-D points.

SUB PROJPERS(vseg3%,voff3%)
PROJPERS performs one-point perspective projection conversion on
a set of 3-D points.


-------------------------------
SIMULATING NEAR VAR-LEN STRINGS

Declare the routine replacing $ with a % and BYVAL
DECLARE FUNCTION DRAWSTR%(mode%,BYVAL doff%,x0%,y0%,fg%,bg%,gap%)
                                ^^^^^
Define a structure that will be stored in DGROUP.
TYPE SIMSTRtype
length AS INTEGER
addr   AS INTEGER
strg   AS STRING * 200   'or whatever max length you want
END TYPE
DIM SIMSTR AS SIMSTRtype

text$ = "I'M REGISTERING QB/EVGFX, NOW!"  'pretty soon, then?
SIMSTR.strg = text$
SIMSTR.length = LEN(text$)
SIMSTR.addr = VARPTR(SIMSTR.strg)
nx = DRAWSTR(0,VARPTR(SIMSTR),0,0,7,0,8)



All orders include the respective programmer's manual.  Upgrades
are available at the difference in price plus $10.  All orders
will receive update notices unless request is made otherwise.

No credit card orders accepted. Phone only for information.




                           QB/EVGFX v1.1 ORDER FORM


                                                      Qty     Extended

      QB/EVGFX basic  . . . . . . . . . . . $20.00 x _____ = __________

 OR,  QB/EVGFX basic + 2-D windows  . . . .  40.00 x _____ = __________

 OR,  QB/EVGFX basic + 2-D + 3-D windows  .  60.00 x _____ = __________

      Additional products:
         FONTED and 70 fonts .  . . . . . . $20.00 x _____ = __________

                                                  Subtotal:  __________

              (Texas residents only add 8.25%)   Sales tax:  __________

      SHIPPING COSTS   USA   CDN   Foreign  Shipping costs:  ___0.00___
                      none   none   none
                                                     TOTAL: $
                                                             ==========
      Please remit TOTAL amount in US funds on US bank only, to:

        Cornel Huth                    |Foreign order may send US currency
        6402 Ingram Rd.                |via Registered mail--be sure to
        San Antonio, TX  78238-3915    |endorse as AirMail in any case.
        U.S.A


      Name: ___________________________________________________________

      Mailing address: ________________________________________________

      _________________________________________________________________

      _________________________________________________________________

      _________________________________________________________________

      Special instructions or comments (continue on reverse if needed):



      Please indicate how you obtained QB/EVGFX. If from a BBS please
      indicate which one and its telephone number:

      _________________________________________________________________

      BBS:_____________________________ Tele: (     )______-___________

 Opt. CPU:________   O/S:______________  RAM:____________ HD:__________

      What software would you like to see:_____________________________