COMPLEX.BAS & COMPLEX.DOC   
By Rich Geldreich
For any questions, problems, or suggestions:
410 Market St.
Gloucester City, New Jersey 08030
(609)-456-0721

December 27, 1991
     
     This download contains a QuickBASIC 4.5 program that
controls the complex sound generator on many Tandy 1000
computers(The Sx,Rl,Rlx,Hx,Tl,Tl/2, etc.).  It gives much
more sound control to QuickBASIC users than the simple,
mediocre, common SOUND statement. You get 4 voices- 3 tone
and 1 noise. You may control the volume of any of the voices.
All with a couple easy to use subprograms.


             Here are what the subprograms do...


1. SoundOn - no parameters
     Enables sound. Must be executed before any other sound
control statement.

2. SoundOff - no parameters
     Turns all sound off.

3. Volume (Channel,Amplitude)
     Sets the volume of a channel.
     Channel ranges from 1-4. 1-3 being the voice channels,
and 4 being the noise channel. Anything other than 1-4 is
ignored.
     Amplitude ranges from 0-15. 0 being the loudest, 15
being totally silent. Amplitude is logically AND'd with 15,
so anything other than 0-15 does not create an error.

4. Tone (Channel,Count)
     Sets the frequency of a channel.
     Channel ranges from 1-3. Anything other than 1-3 is
ignored.  Count ranges from 1-1023. 1 is the highest
frequency and 1023 is the lowest.  Count is logically AND'd
with 1023 so anything other than 1-1023 does not create an
error.

5. Noise (Shift,FB)
     Controls the noise channel.
     Shift ranges from 0-3.
     FB ranges from 0-1.


                     ÚÄÄÂÄÄÄÄÄÂÄÄÄÄÄÄÄÄ¿
                     ³FB³SHIFT³ TYPE   ³
                     ÃÄÄÅÄÄÄÄÄÅÄÄÄÄÄÄÄÄ´
                     ³ 0³ 0 0 ³Periodic³ N/512
                     ³ 0³ 0 1 ³Periodic³ N/1024
                     ³ 0³ 1 0 ³Periodic³ N/2048
                     ³ 0³ 1 1 ³Tone 3  ³
                     ³ 1³ 0 0 ³White   ³ N/512
                     ³ 1³ 0 1 ³White   ³ N/1024
                     ³ 1³ 1 0 ³White   ³ N/2048
                     ³ 1³ 1 1 ³Tone 3  ³
                     ÀÄÄÁÄÄÄÄÄÁÄÄÄÄÄÄÄÄÙ
     N is the clock frequency that is fed to the complex
sound generator, which is 3,579,545 Hz (a T.V. "colorburst"
crystal).
     Periodic noise is a gritty, low frequency type of noise.
White noise is like the type of noise you get when you tune
to a blank spot on your ancient rabbit-ears type TV. Tone 3
means that the noise channel's frequency is derived from
whatever frequency tone 3 is currently set(this is the most
useful setting because the frequency of the noise can altered
for strange effects).
     The values passed aren't checked, so values other than
0-1 and 0-3 may produce some unexpected results.

6. GetFrequency (Hertz)
     Returns the count needed to be sent to a tone channel to
achieve a certain frequency. Don't use this in tight loops-
because it isn't that quick!
     For instance, Tone 1, GetFrequency(1000) will set channel 1
to 1,000 hertz. Tone 3, GetFrequency(12345) will set channel 3
to 12,345 hertz. Most people can't hear above 10,000 hertz or
so. Also, the lowest frequency that can be set is about 109
hertz.


Notes:
     While the Tandy complex sound chip is pumping out tones-
 the normal QB SOUND command still works! So you really have
5 voices!
     Don't take my examples as good ones-I only spent 15 minutes 
working on them. Experiment!
     All of this information was obtained from the book
"Graphics and Sound for the Tandy 1000s and PC Compatibles"
by William Barden, Jr." (It was sold at Radio Shack.) Or, 
for even more information, get a copy of the technical reference
manual from Tandy national parts for your computer(make sure
you have a heap of money first-mine cost mucho dollars!!!
What a rip!!!)