PrintCAD 1.14

                        resident ADI/HP-GL pen plotter emulator
                              for use as a printer driver
                                with MS-DOS CAD packages
                           including AutoCAD and Microstation


                      (C) Copyright Ravitz Software Inc. 1991,1992



              Ravitz Software Inc.                    BBS/FAX 606-268-0577
              P.O. Box 25068
              Lexington, KY  40524-5068
              USA                          Compuserve 70431,32 Cary Ravitz

                                                                              


                                                                            p-1
         Contents -------------------------------------------------------------

           Introduction ..................................................... 2
           License and Registration                                           3
           What Is New ...................................................... 3
           Operation                                                          4
           Installation ..................................................... 5
           Suggested Startup .BAT Files                                       5
           Syntax ........................................................... 6
           Overview of Options                                                7
           /1, /2, /3, /4, /5 - Alternate Configurations .................... 7
           /A - Location Option                                               7
           /B - Tiling Option ............................................... 8
           /C - Pen Color Option                                              8
           /D - Output Destination Option ................................... 9
           /F - Output Format Option                                         10
           /J, /K - Printer Code Prefix, Suffix Options .................... 12
           /L - Page Layout Option                                           13
           /M - Magnification Option ....................................... 14
           /O - Origin and Orientation Option                                14
           /P - Intercept Mask Option ...................................... 14
           /Q - Number of Copies Option                                      16
           /R - Internal Resolution Option ................................. 15
           /S - Pen Shading Option                                           15
           /T - Temporary File Option ...................................... 15
           /W - Pen Width Option                                             16
           /X - Control Option ............................................. 16
           /Z - Chord Angle and Enhanced Font Option                         16
           Large Paper ..................................................... 17
           Answers                                                           18
           Useful Prefix and Suffix Codes .................................. 19
           Printers                                                          20
           PCX and Fax Output .............................................. 24
           Compatibility and Technical Information                           24
           User Support .................................................... 25
                                                                              


                                                                            p-2
         Introduction ---------------------------------------------------------

           PrintCAD is a pen plotter emulator that acts as a printer driver for
           most IBM/DOS based CAD packages. It lets you print drawings directly
           from CAD programs, via the CAD program's pen plotter driver - either
           AutoCAD's ADI plotter driver or an HP-GL driver.

           PrintCAD works with AutoCAD, AutoSketch, Microstation, Generic CADD,
           Draft Choice, PC-Draft-CAD, and other CAD programs. It will print on
           Epson and IBM 9 pin printers, Epson, Fujitsu, IBM, NEC, and  Toshiba
           24  pin  printers, HP  LaserJet, DeskJet,  DeskJet  500C,  PaintJet,
           QuietJet,  and plotters,  Canon  LBP,  BJ,  and  BJC  printers,  IBM
           LaserPrinter,  ExecJet,  and Quietwriter  2  and 3, Kodak  Color  4,
           Tektronix  ColorQuick, and PostScript printers, and it will generate
           PCX files.

           PrintCAD outperforms most  native CAD printer  drivers and  provides
           additional  flexibility, such as pen width, shading, and color (with
           color  mixing), and  paper  size,  orientation,  magnification,  and
           positioning.  PrintCAD  uses the best graphics modes  available  for
           each printer that it supports.

           PrintCAD  is a swapping resident program that uses 5K of base memory
           and  400K of EMS or XMS memory.  Either 400K of EMS or XMS memory is
           required.  EMS and  XMS are expanded and extended  memory management
           protocols that are typically set  up with memory management software
           such as HIMEM/EMM386, QEMM386, or  386MAX.  If you have  a  computer
           with extended  or expanded memory hardware, you need to install such
           a driver to use it as EMS or XMS memory.

           PrintCAD  automatically loads high if a 5K DOS  or XMS  upper memory
           block is available. You do not need to use LOADHI or LOADHIGH.

           For  use with DOS extender based  programs such as  AutoCAD  386 and
           Microstation  4, a VCPI handler  needs to be present.  VCPI handlers
           are built into MS-DOS  5's  EMM386.EXE and  recent  versions of QEMM
           386, 386MAX, and other 386 memory managers.  If PrintCAD notes "VCPI
           not  present"  then you  need  to  upgrade  your  memory  management
           software.

           PrintCAD has been  tested  in  a  variety of environments.  However,
           because  it is a  swapping resident program, unusual  situations may
           cause it to crash  the  system.  Please  test it thoroughly on  your
           system  before  using it with unsaved data.  PrintCAD  has not  been
           tested under Microsoft Windows, and you should not expect it to work
           in this environment.

           This program is produced by a member of the Association of Shareware
           Professionals (ASP).  ASP wants to  make  sure  that  the  shareware
           principle  works   for  you.   If  you   are  unable  to  resolve  a
           shareware-related  problem  with  an ASP  member  by  contacting the
           member directly, ASP may be able to help. The ASP Ombudsman can help
           you resolve a  dispute or problem  with an  ASP member, but does not
           provide technical support for members' products. Please write to the
           ASP  Ombudsman at  545  Grover Road,  Muskegon, MI 49442  or send  a
           CompuServe message via CompuServe Mail to ASP Ombudsman 70007,3536.
                                                                              


                                                                            p-3
         License and Registration ---------------------------------------------

           PrintCAD is  provided  as is.  There are  no warranties expressed or
           implied.  PrintCAD  is  a  swapping resident  program that may  have
           problems with Microsoft Windows and unusual DOS environments.

           PrintCAD  is  copyrighted  by  Ravitz Software  Inc.  You  may  copy
           PrintCAD only for use under this license agreement.

           PrintCAD is distributed as shareware.  You may use  PrintCAD without
           charge on a trial basis to determine its suitability for you. If you
           continue to use  it  after  your evaluation,  a $49 registration  is
           requested.  This  registration  covers  use by  a  single person (on
           multiple computers)  or installation  on  a single  computer (may be
           used by a group of people).  There is no  cost to  use a later  1.**
           version after registering any 1.** version.

           You may distribute PrintCAD as a stand alone product if you keep the
           entire   package  together,  unchanged,   including   this   license
           explanation, and do not charge more than $10. You may not distribute
           PrintCAD as part of another product.

           To  register your copy of PrintCAD, send your name, address, and $49
           check to:

             Ravitz Software Inc.
             P.O. Box 25068
             Lexington, KY  40524-5068
             USA

           You  will be sent a printed manual and  current disk (specify 3.5 or
           5.25).  If you previously  registered PrintCAD, you may send  $15 to
           get a current disk and manual.

           Multiuser licenses are $49 for the first copy (with disk and manual)
           and thereafter $40  per  copy  (with  disk and  manual) or  $25  per
           license (without disk or manual).

           For users outside the USA, please make checks payable in US dollars,
           and except  for  Canada,  please  use  a  check  from  a US bank  if
           possible. Don't forget to include your country in your address.

           If you register through a business, be sure to include your name.

         What Is New ----------------------------------------------------------

           v 1.14 - handles 40 pens, color dot matrix output uses true black,
                    PCX output, quiet (/XS turns on sound mode), multiple
                    copies (/Q)

           v 1.12 - Tektronix ColorQuick support, revised shading patterns
                                                                              


                                                                            p-4
         Operation ------------------------------------------------------------

           When PrintCAD  is run  for the first  time,  it installs itself  and
           swaps most  of  its  code  to EMS (expanded memory) or XMS (extended
           memory). Subsequent runs look for the resident copy and send control
           information to it, updating the parameters.

           When resident, PrintCAD intercepts calls to DOS that the CAD package
           makes to output  HP-GL.  This data is used to drive the printer.  To
           make this work, you must tell  PrintCAD how  to recognize that HP-GL
           data is being output from your CAD packages.  Choose a filename mask
           that you can match with your  CAD  package, such as *.PLT.  Set this
           with the /P option (/P*.PLT).  Inside your CAD package, output HP-GL
           (HP 7475, HP 7440/17440, or HP 7550) to a file name that matches the
           mask. PrintCAD intercepts the data and prints the picture.

           For  AutoCAD and  AutoSketch, you can use  ADI for the filename mask
           (/PADI).  Configure AutoCAD for an ADI plotter on interrupt hex 78 -
           up to 40 pens, 1016 dots/inch.  Then all output  to this driver goes
           to  PrintCAD  via interrupt  78.  You can  also  use AutoCAD's HP-GL
           driver - setup is the same as noted in the previous paragraph.

           After making PrintCAD resident, you can verify that it is functional
           by copying an HP-GL file to "pcad" with the DOS COPY command.

           For color output, the CAD package should be configured for a plotter
           with multiple pens  (up to 40),  the CAD  package's  pen  assignment
           table  should be  set  up match  screen colors to  pen  numbers, and
           PrintCAD's /C option should set up to match.

           PrintCAD beeps  the first time  that  it is sent  data  after a file
           open.  If you turn on sound (/XS), PrintCAD causes a high beep after
           swapping in its code and a low  beep before swapping it out,  to let
           you know that it is processing.

           PrintCAD can be used with DESQview (DV). If you load PrintCAD inside
           a  DV window, it will only be visible from that  window.  No special
           steps are needed for this.  If you load PrintCAD  before running DV,
           there may be problems, depending on your configuration.  If you have
           problems, instead of running PCAD  to  install PrintCAD, run PCADDV.
           This  loads PrintCAD at the top  of lower memory, preventing it from
           overwriting DV  code.  You  must  have  a 5K upper memory  block for
           PCADDV  to  work.  Do not use the /XL option with PCADDV as  it will
           cause PCAD's resident block to split lower memory.

           Internally PrintCAD uses two  byte coordinates  on a 1016  dots/inch
           grid. This allows for plots with coordinates of over 30 inches - far
           larger  than  an HP  7475  can handle.  However, if  you  are  using
           PrintCAD to emulate  a large plotter, you may  overflow the internal
           coordinate system.  This condition is not checked, and it will cause
           garbage output.  You can change the  internal resolution to 508 dots
           per  inch (giving  60 inch maximum  plot sizes) with the  /R  option
           (/R508).  This only helps  store the original  plot internally.  The
           next  step in PrintCAD converts these  coordinates  to the requested
           size in the resolution  of the output device,  and these coordinates
           must also fit in the two byte coordinate list.
                                                                              


                                                                            p-5
         Installation ---------------------------------------------------------

           The PrintCAD package includes these files:

             PCAD.EXE  program          PCADDV.EXE  special loader for DESQview
             PCAD.DOC  documentation    README.*    quick information

           To install PrintCAD copy the distribution files to your working disk
           or directory.

           PCAD.EXE  is  a stand  alone executable  file.  There  are no  extra
           printer driver files or overlays.

           PCAD.DOC is this manual. You can print it with "COPY PCAD.DOC PRN".

           PCADDV.EXE is a loader for setting up PCAD underneath DESQview.

           The  README.*  files are not needed to  run  PrintCAD, but they must
           accompany the rest of the files if you distribute the package.

         Suggested Startup .BAT Files -----------------------------------------

           Below  are some sample .BAT files for various situations.  Such .BAT
           files may be used  to start PrintCAD or  change its parameters.  You
           should not start PrintCAD from under a DOS shell, but you can change
           parameters in this situation.

           AutoCAD or AutoSketch, DeskJet or LaserJet IIP/III, 1/1 prints

             PCAD /padi/fi

           AutoCAD or AutoSketch, DeskJet 500C, 1/1 prints

             PCAD /padi/fa/crgbcmyk

             In AutoCAD configure  a  seven pen ADI  plotter and set up the pen
             assignment table so that pens  1..7  have colors red, green, blue,
             cyan, magenta, yellow, black.

           AutoCAD, DeskJet (printer 1), PaintJet (LPT2), plotter (COM1)

             PCAD /p#prn.plt/fi
             PCAD /2/fp/ckrgbcmyk/dlpt2
             PCAD /3/f8/dcom1

             From AutoCAD plot to 1prn, 2prn, or 3prn.

           Microstation, Canon BJ330, 1/1 print, 11x17 paper

             PCAD /p*.000/f7/l10,16,.25,.25/j27 67 0 17

           PC-Draft-CAD, LaserJet II, legal paper, best fit

             PCAD /xa/p*.plt/mf1/fl/j27 38 108 51 65/l7.97,13.25,0,0

             (/XA and/or /XL may be needed for use with PC-Draft-CAD.)
                                                                              


                                                                            p-6
         Syntax ---------------------------------------------------------------

           The calling syntax of PrintCAD is:

             PCAD /option1 /option2 ...

           Spaces between parameters are not required.

           Except for the /X and  /P options, if a given option is entered more
           than once, only the last entry is used.  And if an option is invalid
           (but not incorrect), it is ignored. Only one /X and one /P option is
           allowed.

           If you do  not enter any  parameters, PrintCAD  displays  its option
           reminder screen.

           Below, [  and ] enclose optional suboptions and | separates mutually
           exclusive suboptions. The options and suboptions may be in any order
           except  that  multiple  numeric suboptions are  ordered  and numeric
           suboptions must follow character suboptions where the characters may
           be digits.  "c"  refers to  a suboption character,  "x" and  "y"  to
           suboption  numbers,  "i"  and "j" to suboption  integers, "b"  to  a
           suboption byte, and "f" to a DOS file or device name.

           For numbers (x, y), a decimal point  is allowed but is not required,
           and scientific notation is not allowed.  "-" is allowed but not "+".
           For  integer  input (i, j),  only  base ten  integers from -32768 to
           32767 are allowed. "+" is not allowed. A byte (b) must be a base ten
           integer from 0 to  255 or a hexadecimal  number prefixed with $ from
           $00 to $FF.  Further range checking is done for most options to flag
           unreasonable input.  If an option  has multiple  numeric suboptions,
           these may be separated with commas or blanks.

           ********************************************************************

           It  is very important to choose the right output format (/F option).
           It is likely  that  the  default  output  format will  work on  your
           printer, but it is equally likely  that it  will not produce optimal
           results.  Please look carefully at the entire list of output formats
           before  choosing one, and do not assume that because a  format works
           that it is the best one to use.

           ********************************************************************
                                                                              


                                                                            p-7
         Overview of Options --------------------------------------------------

           PrintCAD's options fall into several categories.  The first is input
           and output  choices.  The input option  (/Pmask) lets you  choose an
           intercept filename mask, or you may select ADI interrupt 78 by using
           "adi". The output options are /F, the output format (printer model),
           and /D, the destination port, device, or file.

           The second category is  the page layout.  /L  controls the size  and
           location of  the print  window (hard  clip limits) and the option to
           box the window. Tiling is set with /B and copies with /Q.

           The third category defines  how the  plot  looks  within  the  print
           window.  /M,  the  magnification,  sets  the size  of  the plot.  /A
           determines the location of the plot within the print window. /O sets
           the  origin  and  orientation, and  is used to rotate or  mirror the
           plot.

           The  fourth category defines the pens, /W for the width,  /C for the
           color, and /S for the shade.

           The fifth category determines how PrintCAD processes the plot.  This
           includes the temporary file /T, the default and minimum chord  angle
           /Z, the internal resolution /R,  and prefix and suffix printer codes
           /J and /K.

           /1, /2, /3, /4, and /5 let you set up multiple configurations.

         /1, /2, /3, /4, /5 - Alternate Configurations ------------------------

           These options select up to 5 alternate configurations, labeled 1..5.
           /1 is  the  default.  The configuration used  for printing is chosen
           based on the file name and mask (/P option).

         /A - Location Option -------------------------------------------------

           /A[O][x,y] - location - default /A

           The A option determines the location of the plot in the print window
           by specifying a point on the plot that is to be aligned with a point
           in the print window.  You can specify the  plot alignment point with
           x,y  in   inches   from  the   plot's   origin  (before   PrintCAD's
           magnification is applied), or let it default to the plot center. For
           the print window alignment point, you can default  to the  center or
           specify the origin with  O.

           /A      puts the center of the plot at the print window center
           /AO0,0  puts the plot 0,0 at the print window origin
           /A0,0   puts the plot 0,0 at the print window center
                                                                              


                                                                            p-8
         /B - Tiling Option ---------------------------------------------------

           /B[i,j,x] - tiling parameters - default /B1,1,0

           /B  lets  you  specify tiling options that break a  large  plot into
           pages. Each page is defined by the page layout option (/L).  I and j
           specify  the number of tiles (pages) horizontally and vertically.  X
           specifies the overlap in inches.

           /B2,2,.5  breaks the plot into 4 pages with .5 inch overlap
           /B        is the same as /B1,1,0 and produces no tiling

         /C - Pen Color Option ------------------------------------------------

           /C[O|T]c.. - color - default /CK

           /C specifies the color  of each of  40 pens.  The colors  are  B for
           blue, C for cyan, G for green, K for  black,  M  for magenta,  R for
           red, W for white, and Y  for  yellow.  Unspecified pens use the last
           selected color  (/CRGB  is the same as  /CRGBBBBBB).  If  the output
           format  does not  allow  color then  nonwhite  colors are changed to
           black.

           Additional colors can be created with shade mixing. These colors use
           shading patterns  to  mix  the  eight pure colors.  The format for a
           mixed color is  .??  where each ?  represents any of  the eight pure
           colors.  The first  color is printed  with the pen's shading pattern
           (/S option)  and the  second  is printed  with  the  inverse shading
           pattern.  If  the shade value is  0 (solid) it is replaced by 2 (one
           pel checkerboard) which produces the most uniform mixed colors.

           Mixed colors need line  widths  of at least  2 (4  for 2 pel shading
           patterns) to look good, and they may have  visual artifacts on edges
           near a 45 degree angle.  Multipass dot matrix formats may not handle
           color mixing well.

           By default, colors are  overwritten into the print,  so they  appear
           opaque.  You can  switch to translucent colors (ored into the print)
           with the  T suboption, and then back to opaque with the O suboption.
           Make  this  mode switch in front of the pen that you want to change.
           For PostScript devices and plotters, the color processing is done by
           the device, not PrintCAD.  PostScript  devices  use opaque lines and
           plotters use translucent lines.

           " means repeat the previous color.

           /CK             sets pen 1..8  to black
           /CKOR.MB""T.KY  sets pen 1     to black
                                pen 2     to opaque red
                                pen 3..5  to opaque magenta on blue
                                pen 6..40 to translucent black on yellow
                                                                              


                                                                            p-9
         /D - Output Destination Option ---------------------------------------

           /D[+]f - destination - default /D1

           The D option specifies the output printer port, device, or file. The
           + suboption causes files to  be appended rather than overwritten (it
           has no effect on device output). 1, 2, and 3 select the BIOS printer
           routines.  X1, X2, X3, and X4 select xon/xoff controlled serial port
           drive.  H1,  H2,  H3, and H4 select hardware controlled serial  port
           drive. You can also use the DOS devices LPT1, COM1, etc.

           PrintCAD cannot set up the serial ports. This is usually done in the
           AUTOEXEC.BAT with MODE (probably MODE COM1:9600,N,8,1,P).

           /D2          sends output to the second parallel port via BIOS
           /DLPT3       sends output to the DOS device LPT3
           /D+TEMP.PRN  appends output to file TEMP.PRN
                                                                              


                                                                           p-10
         /F - Output Format Option --------------------------------------------

           /Fc[-|+|*][!][~][x,y] - output format - default /FN~

           The F option specifies the output format. -, +, and * are resolution
           modifiers, !  selects a  compression mode  driver,  and ~  turns off
           color processing on  color  printers.  -, +, *, !, and ~ are allowed
           even where they have no effect.

           You  may  enter the horizontal and vertical resolution of the output
           device in dots/inch.  This overrides PrintCAD's normal output device
           resolution, but does not affect the  structure of the output  format
           (-,+, and * generally do alter the output structure).  These numbers
           must follow the format character. This lets you compensate for print
           size  error.  For example,  a 360x360 dpi printer consistently under
           indexes so that a  6  inch high  box  comes out 5.94  inches.  Using
           360,363.6 (6/5.94*360 = 363.6) removes the error.

           Drivers marked below with ! have a compression mode driver, selected
           with "!".  This may be  very useful, but it depends on your printer.
           These  drivers compress the  output data by breaking  bit map strips
           with printhead positioning commands.  This  saves data  transmission
           time, but some  printers spend more  time positioning the  printhead
           than is saved by not sending the data.

           A  number of  printers use  compression  mode by default.  It can be
           turned off with ­ (ASCII 173).

           Drivers marked below with ~  are  color devices.  Using ~ suppresses
           color processing, substituting black for all colors except white.

           /F1     ~ IBM 9 pin ....................................... 120x72
           /F1+    ~ IBM 9 pin (2 pass)                                120x144
           /F1*    ~ IBM 9 pin (4 pass) .............................. 240x144
           /F2       IBM Quietwriter 2                                 240x240
           /F3       IBM Quietwriter 3 ............................... 240x240
           /F4-      IBM LaserPrinter (PPDS mode)                      150x150
           /F4       IBM LaserPrinter (PPDS mode) .................... 300x300
           /F5    !~ IBM 24 pin alternate 1                            180x180
           /F5+   !~ IBM 24 pin alternate 1 (2 pass) ................. 360x180
           /F5*   !~ IBM 24 pin alternate 1 (4 pass)                   360x360
           /F6    !  IBM Proprinter X24 .............................. 180x182
           /F6+   !  IBM Proprinter X24 (2 pass)                       360x182
           /F6*   !  IBM Proprinter X24 (4 pass) ..................... 360x364
           /F7-      Canon BJ (Proprinter mode), IBM ExecJet           180x180
           /F7       Canon BJ (Proprinter mode), IBM ExecJet ......... 360x360
           /F8       HP, IBM plotter                                  1016x1016
           /F9    !~ NEC 24 pin ...................................... 180x180
           /F9+   !~ NEC 24 pin (2 pass)                               360x180
           /F9*   !~ NEC 24 pin (4 pass) ............................. 360x360
           /FA-    ~ HP DeskJet 500C, Mannesmann Tally MT92C           150x150
           /FA     ~ HP DeskJet 500C, Mannesmann Tally MT92C ......... 300x300
           /FB-    ~ Canon BJC 800 (Epson LQ mode)                     180x180
           /FB     ~ Canon BJC 800 (Epson LQ mode) ................... 360x360
                                                                              


                                                                           p-11
           /FD-      Canon LBP (ISO mode) ............................ 150x150
           /FD       Canon LBP (ISO mode)                              300x300
           /FF    !~ Fujitsu 24 pin .................................. 180x180
           /FF+   !~ Fujitsu 24 pin (2 pass)                           360x180
           /FF*   !~ Fujitsu 24 pin (4 pass) ......................... 360x360
           /FI-      HP LaserJet 3, DeskJet                            150x150
           /FI       HP LaserJet 3, DeskJet .......................... 300x300
           /FJ-      Canon BJ (BJ130 mode)                             180x180
           /FJ       Canon BJ (BJ130 mode) ........................... 360x360
           /FK     ~ Kodak Diconix Color 4                             192x192
           /FL-      HP LaserJet ..................................... 150x150
           /FL       HP LaserJet                                       300x300
           /FN     ~ Epson 9 pin ..................................... 120x72
           /FN+    ~ Epson 9 pin (3 pass)                              120x216
           /FN*    ~ Epson 9 pin (6 pass) ............................ 240x216
           /FO    !~ Toshiba 24 pin                                    180x180
           /FO+   !~ Toshiba 24 pin (2 pass) ......................... 360x180
           /FO*   !~ Toshiba 24 pin (4 pass)                           360x360
           /FP    !~ HP PaintJet ..................................... 180x180
           /FQ       HP QuietJet (PCL mode)                            192x192
           /FR     ~ Tektronix ColorQuick ............................ 216x216
           /FS     ~ PostScript                                       1016x1016
           /FT    !~ Epson 24 pin .................................... 180x180
           /FT+   !~ Epson 24 pin (2 pass)                             360x180
           /FT*   !~ Epson 24 pin (4 pass) ........................... 360x360
           /FW     ~ Epson 9 pin alternate                             120x72
           /FW+    ~ Epson 9 pin alternate (3 pass) .................. 120x216
           /FW*    ~ Epson 9 pin alternate (6 pass)                    240x216
           /FX    !~ IBM 24 pin alternate 2 .......................... 180x180
           /FX+   !~ IBM 24 pin alternate 2 (2 pass)                   360x180
           /FX*   !~ IBM 24 pin alternate 2 (4 pass) ................. 360x360
           /FZ     ~ ZSoft .PCX                                        100x100
           /FZi,j  ~ ZSoft .PCX ........................................ ixj

           Most 9 pin  printers, including the IBM Graphics Printer,  work best
           with  the /FN  drivers, even  if  they claim Proprinter rather  than
           Epson compatibility.  9 pin printers with 1/144  inch indexing, such
           as the IBM  Proprinter and 2380,  work better with the /F1  drivers.
           And some not fully compatible 9 pin printers only work with /FW, the
           Epson 9 pin alternate drivers.

           Most   Proprinter  X24   compatible  printers,  including   the  IBM
           Quickwriter and 2390, work best with /F5 or /FX. /F6 is only for the
           IBM Proprinter X24, XL24, X24E, XL24E, and 24P.
                                                                              


                                                                           p-12
         /J, /K - Printer Code Prefix, Suffix Options -------------------------

           /J[b,b,..] - printer code prefix - default /J
           /K[b,b,..] - printer code suffix - default /K

           /J lets  you send codes to the printer before PrintCAD's usual  data
           is sent and /K lets  you send  codes after PrintCAD's usual  data is
           sent.  This  lets  you  set  up and reset  the  printer  for special
           situations. These are not needed in the normal use of PrintCAD.

           For  plotter  and  PostScript  output,  the  /J  codes   follow  the
           initialization commands.

           The  codes  are  specified  with  byte  values  (0..255  or $0..$FF)
           separated with blanks or commas.  There is  a limit of 80 characters
           for any option, so very long  sequences must  be handled outside  of
           PrintCAD.

           /J27 79   sets skip perforation off  to allow plots  larger than one
                     page on most continuous form printers
           /K10 10   sends two line feeds after the plot
                                                                              


                                                                           p-13
         /L - Page Layout Option ----------------------------------------------

           /L[B][x,y[,x,y]] - page layout - default depends on printer

           The L option defines the page layout.

           B boxes the plot at the print window edge using pen 8.

           The first optional x and  y are the print window width and height in
           inches rounded to  .01.  These define  the hard  clip limits.  These
           values are not checked against  your printer's capabilities.  If you
           specify a print  window  that exceeds the output  device limits, the
           results are  unknown.  You may need to reset your printer's margins,
           maximum line  length, or  page length to get large plots  (see Large
           Paper). The size needed for a given width and height exceeds x and y
           by 8 pels to allow for line widths.

           The  second optional x and y are the left and top margins,  measured
           from the printer's left margin and current  vertical position to the
           print  window.  The top margin  is  modified  to match the printer's
           native indexing,  but  is  accurate  to  .02 inch.  The  margins for
           HP-GL  and PostScript  are measured  from the  device's  0,0  (left,
           bottom).

           THE PRINT  WINDOW PLUS MARGINS MUST FIT WITHIN THE PRINTABLE AREA OF
           YOUR PRINTER.

           Each printer has a default page layout.  The default print window is
           7.54x10.14  for   printers  and   10.14x7.54  for   plotters.   This
           corresponds to  HP  7440  A size  paper.  The  margins  are  printer
           specific to compensate for different paper  handling.  In evaluating
           user  options,  PrintCAD  processes each  option  and  when finished
           reprocesses the default page  layout for the chosen printer and then
           reprocesses  the  last user /L  option.  This procedure  gives  good
           default  values so that your /L option can change the letter or size
           suboptions and still have good margins.

           /LB7.5,3,.5,0  makes  the  print window 7.5 inches wide and 3 inches
                          high,  with  a .5 inch left margin and no top margin,
                          and boxes the print window
           /L7.54,10.14   sets window equivalent to HP 7440 with A  paper
           /L7.54,10.74   sets window equivalent to HP 7440 with A4 paper
           /L7.84,10.20   sets window equivalent to HP 7475 with A  paper
           /L7.60,10.88   sets window equivalent to HP 7475 with A4 paper
           /L10.20,16.38  sets window equivalent to HP 7475 with B  paper
           /L10.88,15.90  sets window equivalent to HP 7475 with A3 paper
                                                                              


                                                                           p-14
         /M - Magnification Option --------------------------------------------

           /M[F]x - magnification - default /M1

           The M option specifies  the magnification.  F fits the  plot to  the
           print window size.  The default, /M1, gives the same size plot as an
           HP 7475 plotter.

           /MF.9  fits the plot to the print window and shrinks it 10%
           /M1    prints at the same size as an HP 7475
           /M.5   prints at half the size of an HP 7475

         /O - Origin and Orientation Option -----------------------------------

           /O[1|2|3|4[L]] - origin, orientation - default /O1

           The O  option  sets the  print  window origin and  orientation.  The
           origin is one of  four  corners numbered 1..4 for  upper left, lower
           left, lower right, and upper right. The L suboption specifies a left
           handed coordinate system (this should never be needed).

           Here are pictures of PrintCAD's view of the output media compared to
           an HP 7475's view, to help with choosing a /O option.

           HP 7475                                 PrintCAD

           A size           B size                 printer       plotter

             yÚÄÄÄÄÄÄÄÄ¿    0,0ÚÄÄÄÄÄÄÄÄ¿y         ulÚÄÄÄÄÄ¿ur   ulÚÄÄÄÄÄÄÄÄ¿ur
              ³        ³       ³        ³           1³     ³4     1³        ³4
              ³        ³       ³        ³            ³     ³       ³        ³
           0,0ÀÄÄÄÄÄÄÄÄÙx      ³        ³            ³     ³     llÀÄÄÄÄÄÄÄÄÙlr
                               ³        ³            ³     ³      2          3
                               ³        ³          llÀÄÄÄÄÄÙlr
                               ³        ³           2       3
                              xÀÄÄÄÄÄÄÄÄÙ

           /O1  puts the print window's origin in the upper left corner
           /O2  puts the print window's origin in the lower left corner

         /P - Intercept Mask Option -------------------------------------------

           /PADI|mask - intercept mask

           /PADI sets up PrintCAD as an AutoCAD ADI plotter driver. /Pmask lets
           you  choose  a DOS file mask as PrintCAD's intercept mask.  The mask
           should not include disk  or directory information - PrintCAD ignores
           this information when looking at  file names.  The mask may  contain
           the character #.  This is the same as ?, but when a file matches the
           mask   the  character  that  matches  the  #  selects  the  PrintCAD
           configuration - 2..5  selects configurations 2..5  and anything else
           selects configuration 1.

           /Padi       sets up PrintCAD to take data from AutoCAD interrupt 78
           /P*.plt     intercepts data written to *.plt
           /P#prn.plt  intercepts data written to 1prn.plt, 2prn.plt, etc.
                                                                              


                                                                           p-15
         /Q - Number of Copies Option -----------------------------------------

           /Qi - number of copies - default /Q1

           /Q  sets the number of copies of  each printed page.  The default is
           one.  Page printers  produce multiple  copies  faster using  the  "N
           copies" prefix code (see Useful Prefix and Suffix Codes).

         /R - Internal Resolution Option --------------------------------------

           /Ri - internal resolution - default /R1016

           /R sets the internal grid resolution  in dots/inch.  It is  normally
           1016 and rarely needs  to be changed.  To fit very large plots  into
           the   -32768..32767  coordinate  limit,  use   /R508.   Setting  the
           resolution to a multiple  of the output device  resolution times the
           magnification may yield a small improvement in print quality.

         /S - Pen Shading Option ----------------------------------------------

           /Sc.. - pen shading patterns - default /S0

           /S  assigns a shading pattern to each pen.  Unspecified pens use the
           last specified shade.  The shade values are 0..8.  0  is the default
           solid line.  1..4 are 1 dot patterns (75%, 50%, 25%, 12.5%) and need
           line widths of at least three to give good looking  lines.  5..8 are
           2x2 dot patterns  (75%, 50%, 25%,  12.5%) and need line widths of at
           least five to give good looking lines. Some printers, especially dot
           matrix printers  in  multipass modes,  may wash  out shading because
           they have a dot size that is large relative to the dot spacing.

             1     2     3     4       5         6         7         8
             ÛßÛÜ  ßÜßÜ  ßÜ       ß    ÛÛÛÛÛÛ    ÛÛ  ÛÛ    ÛÛ              ÛÛ
             ßÛÜÛ  ßÜßÜ    Üß   ß      ÛÛ  ÛÛÛÛ    ÛÛ  ÛÛ    ÛÛ
             ÛßÛÜ  ßÜßÜ  ßÜ       ß    ÛÛÛÛ  ÛÛ  ÛÛ  ÛÛ          ÛÛ    ÛÛ
             ßÛÜÛ  ßÜßÜ    Üß   ß        ÛÛÛÛÛÛ    ÛÛ  ÛÛ      ÛÛ

           /S024  sets pen 1 to solid, pen 2 to 50%, pen 3..8 to 12.5%

         /T - Temporary File Option -------------------------------------------

           /T[+]f - temporary file - default /TPRINTGL.TMP

           PrintCAD  uses  a temporary file when it does not have enough memory
           to handle  a plotfile.  You can use /T to put it on a RAM  disk  for
           extra speed.  You can force the use of a temporary file, if the plot
           has over  1024 data points, with +.  If you use a RAM  disk this may
           speed printing.
                                                                              


                                                                           p-16
         /W - Pen Width Option ------------------------------------------------

           /Wc.. - pen widths - default /WA

           The W option assigns pen line widths. Each width may be 0..9, .10 ..
           .16 pels or A..I for 2..10 units of 4/1016 inch (.1 mm).  A..I gives
           a  device  independent width, but it is an approximation, limited by
           the device technology. Unassigned pens use the last assigned width.

           For  nonsquare  matrix  printers,  PrintCAD  uses  "pens"  that  are
           optimized for an x/y ratio of .67, 1, or 1.5. The widths are figured
           in the direction of  higher resolution, and are  not accurate in the
           other direction.

           Line widths of over eight pels are  slightly distorted at  the print
           window edge to fit within the four pel border.

           /WA      sets pen 1..40 to 0.2 mm
           /WB2.16  sets pen 1     to 0.3 mm
                         pen 2     to 2 pels
                         pen 3..40 to 16 pels

         /X - Control Option --------------------------------------------------

           /XQ - queries PrintCAD installation
           /XR - removes PrintCAD if allowed
           /X[X][L][A][S] - controls PrintCAD's setup

           /XQ  checks to see  if  PrintCAD is installed.  /XR removes PrintCAD
           from memory, if allowed. /XQ and /XR disallow all other options.

           The  other suboptions  control PrintCAD's setup, and  are  effective
           only during initial  setup.  X forces the  use  of XMS  for swapping
           instead of EMS.  L forces PrintCAD  to load low  instead  of using a
           UMB.  A sets an alternate handle (use with PC-Draft-CAD and Drafix).
           S adds progress  beeps.  These may be used in any combination.  Each
           one, except S, may or may not improve compatibility.

           /XL  sets up PrintCAD in low memory

         /Z - Chord Angle Option ----------------------------------------------

           /Z[E]i,j - default, min chord angle, enhanced font - default /Z10,5

           The  Z  option  specifies the default  and  minimum chord angles for
           circles and arcs. The HP 7475 defaults to a chord angle of 5 with no
           minimum. But using chord angles of less than 10 returns little print
           quality  improvement and takes a lot  of  processing  time.  So  the
           default Z option is /Z10,5. For better emulation use /Z5,2.

           The  E suboption  says to use the enhanced font,  which  doubles the
           number of chords on curves in text, improving the  curve smoothness.
           This is only effective on character heights above .5 cm. And for CAD
           packages  (including  AutoCAD)  that  use  vectors  to  create  text
           (instead of the HP-GL label command), this option is ineffective.

           /Z5,2  sets the default chord angle to 5 degrees, the minimum to 2
                                                                              


                                                                           p-17
         Large Paper ----------------------------------------------------------

           PrintCAD can handle printing on  paper larger than the usual 8.5x11,
           but  this  takes  some  extra  work.  First  you  need  to  increase
           PrintCAD's print window to cover the large paper.  This is done with
           the /L option.  The  print  window plus the  margins  (/L)  must fit
           within the printer's printable area.

           And  then you must make sure that your printer recognizes the larger
           paper  height.  For  continuous forms  paper  this is best  done  by
           setting skip perforation to  off,  either by printer switch or  with
           PrintCAD prefix codes.  For Canon, Epson, Fujitsu, IBM, and NEC line
           printers (dot matrix, ink jet, thermal) use /J27 79.

           For  cut sheet paper, on  Canon,  Epson, Fujitsu,  IBM, and NEC line
           printers use /J27 67 0 n, where n is the page length in inches.

           For  page printers,  legal  size paper  may be specified with  these
           printer  code  prefixes: HP-PCL printers /J27 38 108 51  65 (/K27 38
           108 50 65 to reset  to 11 inch paper), Canon LBP printers /J27 91 51
           50 59 59 112 (/K27  91 51 48 59 59 112  to  reset), IBM LaserPrinter
           /J27 91 70 5 0 3 1 2 1 (/J27 91 70 5 0 3 1 1 1 to reset).

           To  get a 10x16  print  window on  11x17  paper with a Canon, Epson,
           Fujitsu, IBM, or NEC line printer, use these options: /L10 16 .4 .25
           /J27 67 0 17.  You will probably need to adjust the margins (.4 .25)
           for best centering.

           The  maximum  width  of  the print  window on  most  narrow carriage
           printers is 8  - 8/(horizontal dpi).  For 300 dpi printers,  this is
           7.97.  At 120 dpi it is 7.93.  The maximum width of the print window
           on most wide carriage printers is 13.6 - 8/(horizontal dpi).  At 180
           dpi this is 13.55.  At 360 dpi  it is  13.57.  The  horizontal print
           margin should be set to 0 to get this width.
                                                                              


                                                                           p-18
         Answers --------------------------------------------------------------

           To get data from your CAD package to PrintCAD you must PLOT.  Do NOT
           print.

           If you are getting system  crashes or nothing from PrintCAD, try the
           options /XA, /XX, /XL, /XAX, /XAL, /XXL, and /XAXL.

           If  your plot is messed up, with wraparound lines covering the page,
           you have probably  exceeded the PrintCAD  internal coordinate limit.
           This happens when the HP-GL coordinates exceed 32 inches. Reduce the
           internal resolution  with /R762 for  coordinates up to 42  inches or
           /R508 for coordinates up to 64 inches.

           To get color output from PrintCAD, you must:

             Define a multipen plotter in your CAD package.

             Set  up  the pen assignment table in your CAD package so that each
             color is assigned to a pen.

             Use the PrintCAD /C option to assign the same colors to PrintCAD's
             pens, for example /CRGBCMYK.

           Plot spoolers are not  generally compatible with PrintCAD, and would
           be of little value if they were.  If it worked, a plot spooler would
           send  data  to  PrintCAD the background,  but PrintCAD's  processing
           would take place in the foreground.

           Print buffers  may or may not be compatible with PrintCAD.  You must
           install the buffer first.

           If your prints are coming out not quite to scale:

             For ADI plotters,  check  that your  plotter  is  defined  as 1016
             steps/inch.

             Check that no calibration is being done by the CAD package.

             See  /F  Output  Format  Option  for  information  on  print  size
             correction.

           For the Canon  BJC-800, the right margin defaults to  8 inches.  Use
           /J27 81 114 to set it to 11.4 inches. Because the margin can only be
           set once  between printer resets, you may need to use /J27  64 27 81
           114 (27 64 is a printer reset).

           For the Canon BJ-330 and most  other wide  carriage PC printers, the
           maximum  print  window width  is 13.57  inches.  This is  a  printer
           limitation that you cannot get around.
                                                                              


                                                                           p-19
         Useful Prefix and Suffix Codes ---------------------------------------

           Below,  n  represents any number 0..255, nA represents any number in
           ASCII format (1 becomes 49, 2 becomes 50, 43 becomes 52 51, etc.)

           Canon, Epson, Fujitsu, IBM, NEC dot matrix and inkjet printers
             N inch paper          27 67 0 n
             17 paper              27 67 0 17
             Skip perforation off  27 79
             Reset                 27 64

           HP-PCL printers
             Reset                 27 69
             Portrait mode         27 38 108 48 79
             Top margin 0          27 38 108 48 69
             Skip perforation off  27 38 108 48 76
             11 inch paper         27 38 108 50 65
             14 inch paper         27 38 108 51 65

           HP LaserJet
             N copies  27 38 108 nA 88

           HP DeskJet 500C
             50% shingling  27 42 111 49 81  (1/2 speed, reduced banding)
             No depletion   27 42 111 49 68  (uses more ink, better quality)

           PostScript
             N copies           nA 32 88 67
             Nominal dots/inch  nA 32 88 88  (use with /FS nA nA)

           IBM LaserPrinter
             11 inch paper, tray 1, n copies  27 91 70 5 0 3 1 1 n
             14 inch paper, tray 1, n copies  27 91 70 5 0 3 1 2 n
             14 inch paper, manual, n copies  27 91 70 5 0 1 1 2 n
             N copies                         27 91 70 5 0 0 0 0 0 n

           Canon LBP
             11 inch paper          27 91 51 48 59 59 112
             14 inch paper          27 91 51 50 59 59 112
             Manual feed            27 91 49 113
             Automatic feed         27 91 48 113
             Full page memory mode  27 59 27 91 50 38 122
             N copies               27 91 nA 118
             Cursor to top of page  27 91 48 100
             Diablo mode            27 58
             ISO mode               27 59

           HP QuietJet
             HP-PCL mode      27 37 65
             DIP switch mode  27 37 64
                                                                              


                                                                           p-20
         Printers -------------------------------------------------------------

           Canon BJ and BJC Printers, IBM ExecJet

             For  the BJ130e,  BJ10e, BJ10ex,  BJ300,  BJ330,  and  ExecJet  in
             Proprinter mode, use /F7.  This is the fastest way to  drive these
             printers at 360 dpi.

             /FJ gives 360 dpi graphics for any Canon BJ printer in BJ130 mode.
             The printer is set to 10 pitch text.

             You can use /FT*! with the BJ or ExecJet printers in Epson LQ mode
             to get 360 dpi print, but it is very slow.

             These printers  have an image  density option (switch  1-9 on  the
             BJ130,  1-4  on  the  BJ300,  BJ330,  and  ExecJet).  Low  density
             eliminates  every second pel.  To get the full 360 dpi resolution,
             use high density.  For the BJ300, BJ330, and ExecJet, also be sure
             that the front panel FONT HQ (high quality) light is on.

             For Canon BJC printers, use /FB in Epson LQ mode. This driver uses
             a graphics mode that is not supported by the BJ printers.

           Canon LBP Printers

             /FD  works  with any Canon LBP printer in ISO mode.  At 300 dpi it
             takes up to one  meg  of  printer memory to print a full  page  of
             graphics. At 150 dpi (/FD-) 512K handles a full page.

             It  may help to set the printer memory mode with /J27 59 27 91  50
             38 122.

             If the printer  is in Diablo mode, PrintCAD switches to  ISO mode.
             To switch back to Diablo mode on completion, use /K27 58.

           Epson, IBM 9 Pin Printers

             /FN, /FW, and /F1 cover a wide range of Epson/IBM compatible 9 pin
             dot matrix printers.  You need a  cyan/magenta/yellow/black ribbon
             to get color prints. The * drivers use 1/240 graphics. /FN+, /FN*,
             /FW+,  and  /FW*  use  1/216  indexing  and  do  three  vertically
             interleaved passes.  /F1+  and /F1* use  1/144 indexing and do two
             vertically interleaved passes. /FW sets line feeds to 1/6 inch.

             For Epson printers,  the IBM Graphics  Printer, and other printers
             with 1/216 indexing hardware, /FN is preferred. For some not quite
             compatible  printers, /FW works.  For  IBM  Proprinters  and other
             printers with 1/144  indexing hardware, /F1  gives better results.
             Some Proprinters do not handle 1/240 graphics correctly.

             These drivers use the following escape codes:

               esc 3  set n/216 line feeds for all /FW
               esc J  index n/216 (n=2 for 1/144 index) for all /FN and /F1
               esc L  graphics command for /FN, /FN+, /FW, /FW+, /F1, and /F1+
               esc Z  graphics command for /FN*, /FW*, and /F1*
               esc r  set ribbon color (only if color is specified)
                                                                              


                                                                           p-21
           Epson, Fujitsu, NEC, Toshiba 24 Pin Printers

             /FT  covers  all  Epson LQ printers and  many  compatible printers
             (Panasonic in LQ mode and others).  /FF works with  Fujitsu 24 pin
             printers in Fujitsu mode.  /F9 works with NEC 24 pin printers. /FO
             works  with Toshiba 24  pin printers.  /FO  resets the  line  feed
             distance to 1/6 inch on completion.

             For all of  these  drivers, you  need  a cyan/magenta/yellow/black
             ribbon to get color prints. The + and * drivers use 1/360 graphics
             mode,  and  the * drivers use 1/360  (1/120 for /FO*) indexing and
             reset the line  feed distance to 1/6 inch on completion.  A  clean
             paper path with  equal tension on  each side  is  needed  for good
             360x360 graphics.

             Many 24 pin printers are not capable of 360x360 graphics and a few
             cannot handle 360x180 graphics.

             The compression mode drivers  (! suboption)  may or  may not be an
             improvement with these printers.

             The /FT drivers use the following printer escape codes:

               esc $    absolute tab
               esc * '  graphics command for /FT
               esc * (  graphics command for /FT+, /FT*
               esc +    set n/360 indexing for /FT*
               esc 2    set 1/6 indexing for /FT*
               esc J    index n/180 for /FT, /FT+
               esc r    set ribbon color (only if color is specified)

             /FT does  not work with IBM Proprinter  X24s in alternate graphics
             mode because it uses the esc $ command.

           HP DeskJet, Mannesmann Tally MT92C

             /FI works with any black/white DeskJet in portrait mode.

             /FA drives the DeskJet 500C or MT92C, and any color 300 dpi HP-PCL
             printer that supports data transfer mode 2.

           HP LaserJet

             /FL works with any LaserJet  compatible printer in portrait  mode.
             Portrait mode  may be set with /J 27 38 108 48 79 or you can reset
             the printer with /J 27 69.

             /FI works with the LaserJet 3 and any HP-PCL 5 compatible printer.

             LaserJets with under one meg of memory may not be able to handle a
             full page of graphics.  /FL uses less printer  memory than /FI, so
             it may be preferred on LaserJet 3s with limited memory.
                                                                              


                                                                           p-22
           HP PaintJet

             /FP drives PaintJet  printers.  PaintJet  printers  are  sold with
             either a serial or parallel interface.  The  parallel interface is
             faster.

             The  compression mode  driver (/FP!)  uses  data  transfer  mode 2
             (instead of 1) and works only with a PaintJet XL.

           HP QuietJet

             /FQ works with QuietJets  in HP-PCL mode.  /J27  37 65  /K27 37 64
             sets HP-PCL  mode and  resets  to  the DIP switch selected mode on
             completion.

           IBM LaserPrinter

             /F4 drives any LaserPrinter in PPDS (native)  mode.  /FL will work
             if the LaserPrinter is in HP LaserJet mode, but this may be slower
             than  PPDS mode.  At  300 dpi it takes up to  one meg  of  printer
             memory  to print a full page of graphics.  At  150 dpi (/F4-) 512K
             handles a full page.

           IBM 24 Pin Printers

             PrintCAD has  three drivers that  cover Proprinter  X24 compatible
             printers. The printers should be in native mode (not AGM).

             The first driver, /F6, is for all IBM Proprinter X24s and the 24P.
             These printers do  1/144 inch indexing, and using them at 180  dpi
             results  in horizontal  white streaks  every  2/3  inch.  The  /F6
             drivers  compensate  for  this by indexing  19/144 inch  per line,
             giving  182 dpi.  To work properly, the printer must be on a  1/72
             boundary when the graphics are printed.  If you keep the line feed
             distance  a multiple of 1/72 (1/6, 1/8, 1/9) then this will always
             be the case.

             The second X24 compatible driver is /F5 and  is referred to as X24
             alternate 1.  This is for printers that are  X24 compatible except
             that they  do 1/180 inch indexing.  This is probably the case with
             most  X24 compatible printers, including the  IBM  Quickwriter and
             IBM 2390  and 2391.  /F5* works only with printers that can handle
             1/360  indexing,   including  the  2390  and  2391   but  not  the
             Quickwriter.

             The third  X24 compatible  driver is /FX and is referred to as X24
             alternate  2.  This is  the same  as  /F5 except that the vertical
             units command uses  a  different  format  that is not strictly IBM
             compatible.  This driver works  with Panasonic 24 pin  printers in
             X24 mode.

             The compression mode drivers (!  suboption)  may or  may not be an
             improvement with these printers.

             Proprinter X24 and XL24 printers are very slow with graphics.  The
             X24E and XL24E are significantly faster.
                                                                              


                                                                           p-23
           IBM Quietwriter 2 and 3

             /F2 and /F3 drive  the Quietwriter 2 and 3.  Do not use  1 for pen
             widths because  Quietwriters do not  print consistent 1 pel lines.
             These  drivers  reset  the  line  feed distance to  1/6  inch upon
             completion.

           Kodak Diconix Color 4

             /FK drives the Color 4.

           PostScript Printers

             /FS outputs PostScript.  All characters, arcs, fill, and clips are
             converted to simple vectors.

             PrintGL's pen color  and  shading parameters  are mapped into gray
             levels or RGB color levels.

             You  can  specify the nominal resolution of  the PostScript with a
             prefix code that includes  the  dots/inch followed  by ' XX'.  For
             example  /J 54 48 48 32 88 88 sets 600 dpi.  The actual resolution
             should be set to match, for example /FS 600,600.

             You can specify the number of copies similarly with the  XC macro,
             for example /J 50 32 88 67 makes 2 (ASCII 050) copies.

           Tektronix ColorQuick

             /FR drives the ColorQuick.

           HP and IBM Pen Plotters

             /F8  outputs low level HP-GL, converting characters,  arcs,  fill,
             and clips to vectors. The output is HP 7440 compatible, containing
             only IN, SP, IW, LT, PU, PD, and PG commands.

             PrintCAD uses its width parameter  (/W) as a  pen selector, so for
             each pen in the  original plot,  you may specify a new pen  in the
             output. The default /W option is /W12345678 for this case. Shading
             and color parameters are ignored.
                                                                              


                                                                           p-24
         PCX and Fax Output ---------------------------------------------------

           Use /FZ to  output a Zsoft PCX bit map.  The horizontal and vertical
           dots/inch  may  be appended  to  override  the default 100x100,  for
           example /FZ80,80. Such output should generally be directed to a file
           with the /D option.

           Since most fax boards  can take  PCX files as input, this is  useful
           for faxing drawings. Use /FZ200,196 to match the fax resolution.

         Compatibility and Technical Information ------------------------------

           PrintCAD  will  run on any IBM compatible DOS computer with  400K of
           EMS or 400K of XMS and a base memory region of 304K. Because it is a
           swapping  resident   program,  it   may   have   problems  in   some
           environments.  PrintCAD  can handle  VCPI (Virtual  Control  Program
           Interface) based DOS extenders, but DPMI based programs (MS Windows)
           and stand alone DOS extenders may cause problems.

           When  using  a DOS extender based  program such  as  AutoCAD  386 or
           Microstation  4,  use   an  extended/expanded  memory  manager  that
           provides VCPI, such as MS-DOS 5's EMM386.EXE/HIMEM.SYS, QEMM 386, or
           386MAX.

           PrintCAD  is a TSR that takes over interrupt hex 21 and  watches for
           DOS 2.0+ file management open functions.  If the filename on an open
           command matches either "pcad" or  the mask specified with  /P,  then
           file  handle dec 99 (or dec  15 if  /XA  is  used) is  returned  and
           PrintCAD is awakened. It then responds to write, device information,
           close functions, seek, and set date functions.

           When awake,  PrintCAD stores HP-GL commands (from the write command)
           until  its  buffer limit (16K) is reached and then  it swaps  in its
           304K memory space, processes the data, and swaps the original memory
           back.

           PrintCAD  was  written by Cary Ravitz and  compiled  with  Borland's
           Turbo Pascal 6.0.  PrintGL Printer Driver  is used  as  the graphics
           engine.
                                                                              


                                                                           p-25
         User Support ---------------------------------------------------------

           The  quickest  way to  resolve  problems with PrintCAD is to use the
           support bulletin board.  The Ravitz Software support  bulletin board
           is at:

             606-268-0577  1200/2400,N,8,1  24 hours/day.

           To ask a question (or make a comment or suggestion), first prepare a
           file with the details of your question. Please be very specific, and
           include  any related information  on  your  hardware,  software, and
           operating environment.  Then call the bulletin board  and choose the
           upload question  option.  XMODEM file  transfer protocol is required
           for this.  Your question will be assigned  a number (such as 1015) -
           remember this number. An answer file (with the assigned number) will
           be posted, usually within 24 hours.

           To  get an  answer,  call the  bulletin  board, choose the  download
           option, then the answer option, and then enter  the  answer  number.
           XMODEM is also required for downloading answers.

           All question and answer files are public.

           You may send questions to Compuserve - 70431,32  Cary Ravitz.

           You may send questions by mail to:

             Ravitz Software Inc.
             P.O. Box 25068
             Lexington, KY  40524-5068
             USA

           Please send  a diskette  (360K, 1.2M, 720K,  or 1.44M, 720K is best)
           with your question  so that example  files or newer  versions of the
           software may  be  included  with the  response.  Return  postage  is
           appreciated.