ScanPlot - Plot Range Finder

                            John Intorcio


This little program is meant as a tool for finding the maximum and
minimum coordintes used in an HPGL or DM/PL plot file created by
AutoCAD.

The synatx is:

                SCANPLOT <Filename>

Extensions are not allowed, .PLT is assumed.

Upon invocation, ScanPlot reports the assumed langauge of the plot file
and begins scanning the commands contained therein.  It gives a vector
count to the screen so you can see that it's working.

On completion, ScanPlot returns the maximum and minimum points that are 
used in the plot file.

ScanPlot can be used with PlotManager to determine the high and low 
plotting ranges for a given plotter.  To use ScanPlot with PlotManager, 
begin by creating two AutoCAD drawings.  Each of these drawings should 
contain a single rectangle.  The first rectangle should be much wider 
than high and the second, much higher than wide.  The idea is to make 
the width the constraint on establishing extents on one and the height 
the constraint on the other.

Next configure AutoCAD for the plotter model and sheet size in question 
and plot each drawing to a file plotting extents and choosing the "Fit" 
scaling option.  You might want to call these plots H and V for 
Horizontal and Vertical rectangles.

Now run ScanPlot on each of the plot files.  The plot file created from 
the Vertical rectangle will yield the maximum and minimum Y values and 
the plot file created from the Horizontal rectangle will yield the 
maximum and minimum X values.

You get the numbers like this:

        Vertical rectangle plot:

            Low Range:      ?,Minimum Y Value
            High Range:     ?,Maximum Y Value

        Horizontal rectangle plot:

            Low Range:      Minimum X Value,?
            High Range:     Maximum X Value,?

These values may then be used in defineing new plotters either by 
editing PlotManager's emulation file or through the interactive 
dialogue.