The Tubesheet Helper v1.0   Evaluation Copy             December 18, 1991




















                          TEMA Tubesheet Builder































                             By: CADsultants
                               PO BOX 5364
                           Deptford, N.J. 08096
                                  U.S.A
                              (609) 384-1378




The Tubesheet Helper v1.0  Demo Version                December 18, 1991



Table of Contents ------------------------------------------------(1)

Copyright --------------------------------------------------------(2)

Shareware Concepts -----------------------------------------------(2)

Limited License --------------------------------------------------(2)

Registration -----------------------------------------------------(2)

Disclaimer -------------------------------------------------------(3)

Trademarks -------------------------------------------------------(3)

Introduction -----------------------------------------------------(4)

System Requirements ----------------------------------------------(5)

Installation -----------------------------------------------------(5)

Recommended DOS Settings -----------------------------------------(6)

Configuring ------------------------------------------------------(6)

How to Run The Tubesheet Helper --------------------------------(7-9)

DXF Importing ----------------------------------------------------(9)

Registration Form -----------------------------------------------(10)



























(c) 1991  CADsultants - CAD/Computer Consultant      Pg 1 of 10


The Tubesheet Helper v1.0  Demo Version                 December 18, 1991



Copyright

Copyright 1991-1992 by CADsultants, All rights reserved. No part of the
publication may be reproduced, transcribed, copied or reduced to any
electronic medium or machine readable form without the written
permission of CADsultants.


Shareware Concept

The Tubesheet Helper is not public domain or free software, but is being
distributed under the shareware concept.  This enables the user to
first use the software before deciding whether or not to purchase it.


Limited License

NON-REGISTERED users of this software are hereby granted a limited
licence for a maximum of 30 days to try this Demo Version on a trial
basis.  Because this is an evaluation, it does not give full support to
all available options. At the end of this trial period, The Tubesheet
Helper must be registered, or use discontinued.


Registration

The registration fee for The Tubesheet Helper is US $395.00 (*).  You
must send US $395.00 (*) to CADsultants for one license per CPU
concurrently using The Tubesheet Helper.  You may register The Tubesheet
Helper only with CADsultants .  No other registrations will be
recognized.  If you are updating from a previous version, registration
will only cost US $95.00 (*).

Please submit all registration and updates using either a printed
copy of the REGISTER.FRM text file included in The Tubesheet Helper
(shareware version) or a photocopy of the registration form at the
end of the document.

If and when you register you will be given the latest version of
The Tubesheet Helper including all the supported options. You also will
receive a printed manual and a serial-numbered copy.



(*) New Jersey State residents please add 7% sales tax.
    Shipping and Handling charges are US $5 and US $10 if outside USA.
    Package will be send UPS Ground, other shipping available at
    additional charge.







(c) 1991  CADsultants - CAD/Computer Consultant      Pg 2 of 10


The Tubesheet Helper v1.0  Demo Version                December 18, 1991



Disclaimer

CADsultants makes no representations or warranties with respect to
this publication or its contents and specifically disclaims any
implied warranties of merchantability or fitness for any particular
purpose. In addition, CADsultants reserves the right to revise this
publication and to make changes from time to time in its contents
without obligations of CADsultants to notify any person of such
revisions or changes.

USE THIS SOFTWARE AT YOUR RISK!


CADsultants
PO BOX 5364
Deptford, NJ
08096 U.S.A.


Trademarks

The Tubesheet Helper is a trademark of CADsultants.
IBM is a trademark of International Business Machines, Inc.
AutoCAD is a trademark of AutoDESK Inc.
MicroStation is a trademark of Intergraph Corp.
TEMA is a trademark of Tubular Exchanger Manufacturer Association, Inc.




























(c) 1991  CADsultants - CAD/Computer Consultant      Pg 3 of 10


The Tubesheet Helper v1.0  Demo Version                 December 18, 1991






Introduction

The Tubesheet Helper is a PC based program for generating full scale Heat
Exchanger Tubesheet layouts in accordance to TEMA. All data is entered
via full screen input sheets.  After data has been entered, the user can
preview the layout On-Screen, then generate a DXF (Data Exchange Format)
file.  The DXF output can be used to import the Tubesheet layout into
your CAD (Computer Aided Design) System for future modification or
plotting.


     *) All Tubesheets can be created per TEMA B, C, or R

     *) Tubesheet data entered via user-friendly input screens

     *) Maximizes number of tubes in a given shell.

     *) Creates Triangular, Rotated Triangular, Square or
        Rotated Square.

     *) Horizontal and Vertical pass partition lanes.

     *) Prints layouts On-Screen.

     *) Generates DXF output files.



























(c) 1991  CADsultants - CAD/Computer Consultant      Pg 4 of 10


The Tubesheet Helper v1.0  Demo Version                December 18, 1991




System Requirements

IBM or 100% Compatible: 8088, 286, 386, or 486
System Memory: 640k or More
Disk Storage: 512k
Floppy Drive: 5-1/4" 1.2Mb, 360k
          or: 3-1/2" 720k, 1.44Mb
Color Monitor: CGA, EGA, or VGA Monitor
MS-DOS: 3.0 or Higher



Installation

Insert The Tubesheet Helper Program Disk in Drive A and enter
the following:

A:
A:\> INSTALL

Installation program will prompt you for a directory to place
support files.

Also Print-out the READ.ME file supplied on your Program Disk for
last minute items not covered in this document.




























(c) 1991  CADsultants - CAD/Computer Consultant      Pg 5 of 10




The Tubesheet Helper v1.0  Demo Version                 December 18, 1991


Recommended DOS Setting

In the Root Directory of your Hard Drive there should be two files
called CONFIG.SYS and AUTOEXEC.BAT. If these files do not exist, t hey
must be created. If they do exist,  compare them to the settings
listed below and make the appropriate changes.

<CONFIG.SYS>
 FILES=20
 BUFFERS=10

<AUTOEXEC.BAT>
PATH=[PATH];C:\TSHELPER

Where [PATH] is the existing path setting, and C:\TSHELPER is the
location you installed The Tubesheet Helper.


Configuring The Tubesheet Helper

There is a configuration file copied with other files in the install
director.  The file TSHELPER.CFG contains values used to set the program
to work with your type of monitor.  Use any ASCII type editor to make
your changes if needed.  Each field in the CFG file is explained on the
previous line in configuration file.

Example:

'The following settings are used to setup your systems monitor type.
'[0]= Text Only and MGA Video
'[1]= CGA and EGA 320x200  16 colors  2 Bits Per Pixel
'[2]= CGA and EGA 640x200  16 colors  1 Bit Per Pixel
'[7]= EGA 320x200  16 colors  4 Bits Per Pixel
'[8]= EGA 640x200  16 colors  4 Bits Per Pixel
'[9]= EGA 640x300  16 colors  4 Bits Per Pixel
'
MONITOR TYPE
9

Lines starting with a single quote (') represents comments.  The line
labeled MONITOR TYPE is the heading for the next line, which in this case
is the number 9.  This sets TSH to display in EGA 640x300 16 color etc...














(c) 1991  CADsultants - CAD/Computer Consultant      Pg 6 of 10


The Tubesheet Helper v1.0  Demo Version                December 18, 1991


How to Run TSH

TSH is easily learned after using it a couple of times.  The first
thing to do is to load TSH,  this is done by entering TSH from the
install directory (C:\TSHELPER).  TSH data input consists of two screens
which allow you to move about each input field sequentially.  Move from
field to field by pressing the arrow up or arrow down keys.  Data fields
can be changed by entering new value over top of old, or by pressing the
delete key. Each of the data fields are described below.

*TEMA Class [B] [C] or [R]:
Sets the Mechanical Standard Class per TEMA Section 1.12

*Tubesheet Outside Diameter:
Self-Explanatory
(VALUE LOCKED AT 25.75" IN DEMO)

*Diameter of Bolt Circle:
*Specifies Tubesheet Bolt Circle if extended for bolting.

*Number of Bolt Holes:
Specifies Number of Tubesheet Bolt Holes if extended for bolting.

*Diameter of Bolt Holes:
Specifies Tubesheet Bolt Hole Diameter if extended for bolting.

*Shell Inside Diameter:
Self-Explanatory
(VALUE LOCKED AT 20.0" IN DEMO)

*Baffle Clearance on Diameter:
Specifies the difference between the Shell I.D. and the Baffle O.D.
If a value of 0 is entered, TSH will default to TEMA Section 4.3

*Outer Tube Limits Diameter:
Specifies the farthest distance from center of Tubesheet to the outside
of an extreme tubehole.  If a value of 0 is entered, TSH will calculate
an O.T.L.  (VALUE LOCKED AT 19.75" IN DEMO)

*Outside Diameter of Tube:
Self-Explanatory
(VALUE LOCKED AT .5000" IN DEMO)

*Choose a Pattern:
Specifies how tube holes shall be placed using standard pattern types as
shown in TEMA Section 2.4.  Patterns can be Triangular, Triangular
Rotated, Square, or Square Rotated.
(VALUE LOCKED AT "Triangular" IN DEMO)

*Tube Pitch:
Specifies the distance between each tube hole on a pattern.
If a value of 0 is entered, TSH will default to TEMA Section 2.5




(c)  1991  CADsultants - CAD/Computer Consultant      Pg 7 of 10


The Tubesheet Helper v1.0  Demo Version                December 18, 1991


How to Run TSH - Continued



*Number of Tie-Rods:
Self-Explanatory
If a value of 0 is entered, TSH will default to TEMA Section 4.71
If a value of -1 is entered, TSH will not place any Tie-Rods.
(VALUE LOCKED AT 8 IN DEMO)

*Diameter of Tie-Rods:
Self-Explanatory
If a value of 0 is entered, TSH will default to TEMA Section 4.71

*Vertical Pass Partition Clearance:
Specifies the distance between the outside of tubes straddling a vertical
pass partition plate or lane.

*Horizontal Pass Partition Clearance:
Specifies the distance between the outside of tubes straddling a
horizontal pass partition plate of lane.

*1st Tube Hole on Tubesheet C/L:
Specifies if the pattern will start with a hole in the center of the
tubesheet or with the pattern straddling.  This value will only be read
if the Horizontal and/or Vertical Pass Partition Clearance=0

*Pattern Offset by Window or Coordinates:
Specifies if the pattern is eccentric to the tubesheet center-line.  The
window option allow you to select an area where not tubes are to be
places.  The pattern will start by placing tubes up to, but not crossing
over the window dimension, then filling the remainder of the tubesheet.
Thereby shifting the pattern. If WINDOW is selected, then the AREA [1]
[2] [3] or [4] must be specified.  Only one window may be specified at a
time.  The areas are as follows:

AREA 1= UPPER Portion of Tubesheet (0)
AREA 2= LEFT Side of TubeSheet (270)
AREA 3= LOWER Portion of Tubesheet (180)
AREA 4= Right Side of Tubesheet (90)

If COORDINATES is selected, then X-Axis and Y-Axis Offset must be
specified.  These values can be any value within the range of the O.T.L.
Direction of offset can be controlled by entering positive or negative
values based on the Cartesian Coordinate System.



*Plot Pattern On Screen:
Allows defined pattern to be previewed On-Screen before creating DXF
file.  If the pattern is not the way you wanted, then you may return to
the input screens to make additional changes.  This process can be
continued indefinitely.



(c)  1991  CADsultants - CAD/Computer Consultant      Pg 8 of 10



The Tubesheet Helper v1.0  Demo Version                December 18, 1991

How to Run TSH - Continued


*Path:
Allows the DXF file to be made in a directory other then the root of the
current drive.  If a path is given it MUST NOT end with a backslash and
specified path MUST EXIST.  (DXF OUTPUT IS NOT AVAILABLE IN DEMO)

*Filename:
Allows you to specify the name of the DXF output file.  Filename must be
8 Characters or less and no extensions are allowed.
(DXF OUTPUT IS NOT AVAILABLE IN DEMO)




DXF Output File


Although DXF output is not available, you will find an actual DXF file
made from the registered version of The Tubesheet Helper.  DXF files have
been tested on AutoCAD Rel 9/10/11, and MicroStation PC v 3.3/4.0.  Here
we will describe the process for loading DXF files in to your CAD System.


**AutoCAD**

Load AutoCAD in your usual way, and stop at the Main Menu.  Enter "1" for
Create new drawing, then the filename you want the pattern to be called,
followed by an equal sign (=).  The equal sign tells AutoCAD not to
reference any prototypes with defined layers, ltypes, fonts, etc.  After
you press enter AutoCAD will load, at the command prompt enter "DXFIN"
followed by the DXF filename.  If the DXF file is not in the current
directory you will need to specify the path as well as the DXF filename.


**MicroStation**

Change directory to USTATION\DXF or wherever your Microstation DXF
directory is located on your system. Enter "DXFIN", then the name you
specified in TSH, followed by the design name you want the pattern to be
called in MicroStation.  After the design file has been created, return
to MicroStation's Main Directory, usually \USTATION. Load MircoStation in
your usual way, and load the design name specified in the DXF process.











(c)  1991  CADsultants - CAD/Computer Consultant      Pg 9 of 10


The Tubesheet Helper v1.0  Demo Version                 December 18, 1991


The registration ownership of The Tubesheet Helper v1.0,  print out and
complete the following form.  Include a check or money order for US
$395.00 (*) to CADsultants for one license per CPU concurrently using The
Tubesheet Helper.  You may register The Tubesheet Helper only with
CADsultants. No other registrations will be recognized. If you are updat-
ing from a previous version, registration will only cost US $95.00 (*).
Send to:


                CADsultants
                PO BOX 5364
             Deptford, NJ 08096
                   U.S.A.

Name: __________________________________________________________________

Title: _________________________________________________________________

Company: _______________________________________________________________

Address: _______________________________________________________________

City: _____________________ Providence: __________ Zip: ________________

Phone: (______) _________________________ Date: ________________________

CAD Software/Version/Machine type:_____________________________________

________________________________________________________________________

How did you receive The Tubesheet Helper v1.0?

__ New Order

__ Friend

__ Upgrade from Version __   -- Serial Number ____________

__ User Group - Group Name ________________________ Phone: ____________

__ Software BBS - BBS Name ________________________ Phone: ____________

__ CompuServe GO ___________ Forum

Comments: __________________________________________________________

____________________________________________________________________

____________________________________________________________________

____________________________________________________________________



(c) 1991  CADsultants - CAD/Computer Consultant      Pg 10 of 10