BLOCKADE (TM)
                    A self checker library for C programs
    
    
    
    
    
    
                    Copyright (C) 1991,92 Indusoft Corp.
    
    
    
    
    
    
    
    
                           Indusoft Corp.
                           PO. Box 26747
                       Greenville, SC 29616-1747
    
    
    





















             Blockade, (C) Copyright 1991-92 Indusoft Corp.  page -1-


    
    
    
    
    
         OVERVIEW
    
         Blockade is a function library for C programmers which allows
         your C programs to protect themselves against unauthorized
         changes. Virus protection IMMEDIATELY comes to mind as its main
         use, but there are more.
    
         I wrote BLOCKADE so that programs I wrote could check
         themselves. Have you had those times too?  Those unexplainable
         times when a program runs but has some odd behavior that makes
         you suspect corruption, virus related or not.
    
         This happened to me when I was checking out a disk caching
         utility. Files I had compiled and linked often quit running
         after copying them to another disk or subdirectory. The
         combination of controller, BIOS, and cache software was
         causing just a few bytes of a file to be altered anytime I
         copied it (and of course without warning or notice).
    
         After several hours of searching, I found the problem and
         looked for a way to make my programs self checking. The result
         was BLOCKADE.
    
         BLOCKADE checks every byte of your EXE or COM to insure that
         changes are detected. Its algorithm is designed to be effective
         but fast enough allow use in your programs.
    
         I also use BLOCKADE in our products to protect against
         unauthorized patches to our programs and to protect our
         customers from running versions of the program damaged
         unintentionally.
    
         Blockade is easy to use.  1 major function analyses your EXE
         file and returns a status code indicating whether your file has
         been altered.

















             Blockade, (C) Copyright 1991-92 Indusoft Corp.  page -2-


    
    
    
    
         NEAT FEATURES
    
         * Fast operation. A 40k EXE file can check itself in less
           than 3 seconds on a 12 MHZ AT.
    
         * Ease of use.  A few #includes and only a handful
           of additions are needed to use BLOCKADE. No changes to
           your program's basic structure are necessary.
    
         * Ability to add user data to a program "skeleton".
           useful for adding custormer names and serial numbers.
         
         * Expandable.  BLOCKADE can be modified to extend the
           number and type checking methods you use.
           The source code to BLOCKADE is available, allowing you to
           create new checking methods unique to your application.
    
         
         THEORY OF OPERATION
    
    
         Blockade works via 2 pieces of code you add to your program.
    
         (1)  A special data structure "SIGNATUR.H", which is #include'd
              in your program.  The structure reserves room for the
              information BLOCKADE will need to analyze your program.
    
         (2)  The function blockade(), which checks your program for
              alteration.
    
         After linking, a special program (BRAND.EXE) is run to find the
         special string included by "SIGNATUR.H" in the data area of
         your EXE file, calculate the checking information and overwrite
         that area with the data blockade() needs to detect changes to
         your file.  Once branded, your program can check itself for
         changes each time it is run.
    
















             Blockade, (C) Copyright 1991-92 Indusoft Corp.  page -3-


    
    
    
    
         I HAVE TO RUN BRAND.EXE  EACH TIME I RELINK MY APPLICATION ?
    
    
         That's the problem I had with other products similar to
         BLOCKADE. The biggest headache was time - it seemed to take
         forever for them to calculate and update my program.
    
         To combat that, ALOT of time went into the all the utilities to
         make things FAST.  For example, on an 8 MHz AT, the Brand
         utility will analyze and brand a 40 K .EXE file in less than 4
         seconds.
    
         The same thing is true for your developed applications. Nobody
         wants to wait 30-40 seconds every time they start your program
         while it self checks.  The check algorithm in BLOCKADE is quick.
         Running from a hard disk, I doubt anyone will notice the delay.
    
         I leave the BLOCKADE code linked in during development - to
         take into account the effect it has on speed and memory use -
         but have the program ignore any error codes until my final
         production link.
    































             Blockade, (C) Copyright 1991-92 Indusoft Corp.  page -4-


    
    
    
         CONTENTS
    
    
         This self extracting file should contain at least the following files:
    
    
         blkade1.c       - the error message function used by BLOCKADE.
         blkdmoms.lib    - Blockade demo library Microsoft 5.1 (Small model)
         blkdmoml.lib    - Blockade demo library Microsoft 5.1 (Large model)
         blkdmots.lib    - Blockade demo library Turbo C 2.01 (Small model)
         blkdmotl.lib    - Blockade demo library Turbo C 2.01 (Large model)
         blkdmobs.lib    - Blockade demo library Borland C++ 2.0 (Small model)
         blkdmobl.lib    - Blockade demo library Borland C++ 2.0 (Large model)
         brand.exe       - calculates your program's checkcode data
                           and "brands" it into your .EXE file.
         demo.c          - Demonstrates use of the Blockade function library.
         demo.exe        - Demo program demonstrating BLOCKADE's use.
         rundemo.bat     - Demonstrates use of the Blockade system.
         mksig.exe       - Generates a SIGNATUR.H file.
         signatur.h      - include file to be embedded in your program.
         blkproto.h      - function prototypes for blockade functions.
         userdata.dat    - a sample user data file used with DEMO.EXE.
         read.me         - any last minute info.
    
         The file BLKDEMO.PAK is an ASCII file listing the exact files
         in this distribution.
    
    
         
         COMPILER'S SUPPORTED
         
         The test drive of BLOCKADE version comes with libraries for
         Turbo C 2.0, Borland C++ 2.0 and Microsoft C 5.x.  I don't know
         if these are usable with Microsoft 6.0.  According to Borland,
         the C++ libraries are NOT reliably usable with Turbo C 2.0.
         However, Turbo C++ and Borland C++ libraries do seem to be
         compatible.
    
         For now, folks with other C compilers must license the source
         code and compile it themselves.  BLOCKADE and all it's support
         programs are written in (almost) ANSI C so things should
         compile up just fine.
         
         The libraries were compiled with the following options.
    
         For TC   :   tc  -O -G -c  -ml(or s)
    
         For BCC  :   bcc -O -G -c  -ml(or s)
    
         For MSC  :   CL /W3 /Ox /Zi  /c /AL(or S)




             Blockade, (C) Copyright 1991-92 Indusoft Corp.  page -5-


    
    
    
         Below is an short program illustrating the BLOCKADE system.
         (This is in fact a section of the DEMO program included in your
         BLOCKADE package)
    
    
    
    
         /* ------------------------------------------- */
    
         #include "blkproto.h"   /* function prototypes              */
         #include "signatur.h"   /* holds the signature string       */
    
         /* ------------------------------------------- */
    
         main(int argc, char **argv)
         {
           char *sp;
           int stat;
    
           printf("Checking myself for changes..\n");
    
           stat = blockade( argv[0], 8000);
    
           printf ("Results of file self check = %d\n", stat);
    
           sp = get_blk_err_msg( stat);
           printf("The status my self check was \"%s\". \n", sp);
    
           return(0);
         }
    
    
         The above example illustrates how easy it is to add self
         checking to your programs.
    



















             Blockade, (C) Copyright 1991-92 Indusoft Corp.  page -6-


    
    
    
    
         Prototype :
    
           int blockade( const char *filename, int buffer_size);
    
    
         Description:
    
         Attempts to open "filename" and analyze it for any alterations.
    
         Allocates "buffer_size"  bytes of dynamic memory for disk I/O
         to improve scanning performance.  Allowable buffer sizes are
         from 512 to approximately 30000 bytes inclusive.  Buffer
         sizes outside this range are set to the closest allowable size
         within the function.
    
         Returns 0 if no changes are detected, else returns a non-zero
         status indicating the reason for failure.  The user's
         application must decide what action to take based on the
         status.
    
    
         Example:
    
    
            include "signatur.h"
            stat = blockade( "DEMO.EXE", 1024);
            if (status != 0)
               {
                 printf(" This file has be altered !!!\n");
               }
    
            Attempts to open DEMO.EXE located int the current directory
            and analyzes it for any changes.  Allocates 1024 bytes of
            dynamic memory for disk I/O to speed things along.
    
            Prints an error message if any alteration if found.
    
            Note: Although the above example if perfectly legal, it is 
            better to use arg[0] rather than a hard coded program name.
            The program's real name is the only one which will work 
            anyway. Arg[0] provides this in all DOS versions 3.0 and 
            above.
    










             Blockade, (C) Copyright 1991-92 Indusoft Corp.  page -7-


    
    
    
         Prototype :
    
           char *get_blk_err_msg( int status );
    
    
         Description:
    
           Returns a READ ONLY pointer to a message relating to
           the "status" code.  This message can then be used to explain
           or document the error to the user.
    
           NOTE: The pointed to string must not be modified.
                 Unpredictable operation may result if modification
                 takes place. Make a copy of this string if you intend
                 to alter it.
    
    
    
         Example:
    
            {
            int status;
    
            status = blockade( arg[0] ,  0);
            if (status != 0)
               {
                 sp = get_blk_err_msg(stat);
                 printf( "%s\n", sp );
               }
            return(status);
            }
    
    
            Attempts to open MYSELF.EXE located in subdirectory
            C:\BLOCK\BIN and analyze it for any changes.
    
            Since 0 bytes (less than the minimum) were specified for
            buffer, the minimum (BLKSIZ bytes) is used for disk
            buffering.
    
            Prints an error message if any alteration if found or if
            file cannot be successfully opened and analyzed.
    











             Blockade, (C) Copyright 1991-92 Indusoft Corp.  page -8-


    
    
         
         Prototype:
    
           void * blk_user_pointer( int *size )
         
    
         Description:
    
           Returns a void pointer to the first char of the user area,
           and the size of that region.
           Use this pointer with its associated size to access your 
           user data inserted when you branded your program.
           Returns NULL if no user area specified.
           Note that your user data can be anytihng, a string, or
           binary data. It is up to you to cast or map it into the
           format you need to use. 
        
         Example:
    
          {
             char *sp;
             void *vp;
             int k, size;
    
             vp =  blk_user_pointer(  &size );    /* Find user string.*/
             sp = (char *) vp;                    /* Cast to char *.  */
             for (k = size; k >= 0 && *sp; k--)   /* Print out the    */
               {                                  /* entire string.   */
                 putch(*sp);
                 sp++;
               }
            }
    
         See demo.c for another example of its use.
    




















             Blockade, (C) Copyright 1991-92 Indusoft Corp.  page -9-


    
    
    
         MKSIG.EXE
    
         "Writes" an include which includes the references and data
         space Blockade needs for operation.  You do not need to run
         MKSIG.EXE unless you wish to change either the reserved data
         size or signature string. However, there's no harm done if
         you do.
    
         MKSIG's syntax is as follows :
    
         MKSIG <"Signature string">   </o>  </us>  </c>
    
         "signature string"
            The text BRAND.EXE should search for to locate Blockade's
            data space. The default is "chk_signature". Note that the
            signature string is case sensitive and spaces do count.
            This string must match the string embedded in SIGNATUR.H.
    
         /us=XXX
    
            Reserve XXX bytes of user data in the blockade reserved 
            area. You must use this option if you intend to add user
            data to the program skeleton prior to branding it.
    
            You may reserve room for user data but are not required to 
            add it when you brand your program.
         
            You may wish to stuff additional info into this region
            such as serial numbers or owner's names.
         
            The maximum user space you may spec is 31,000 bytes.
    
    
         /o=OUTPUT FILENAME
    
            The filename to use in case you don't like SIGNATUR.H.
    
    
         EXAMPLE:
    
             MKSIG  "Brown Fox"  /us=128  /o=BROWN.H
    
          Build a signature array data statement with a signature string
          of "Brown Fox".  Add enough chars to hold 128 bytes of user 
          data.  Write the output to BROWN.H.  The output file is 
          overwritten if it already exists.
    
    






             Blockade, (C) Copyright 1991-92 Indusoft Corp.  page -10-


    
    
         BRAND.EXE
    
         This is the program used to "brand" your program with the
         self-checking info needed at run time. You must BRAND your
         program prior to distributing the program.
    
         Brand's syntax is as follows:
    
         BRAND   filename[.exe]  </s=signature_string> </n> </c>
                                 </uf=USER_FILENAME>
                                 </us=USER DATA STRING>
    
         filename
            The name of the file to brand. The extension .EXE is assumed
            if no extension is specified.  Note that only executable
            programs may be branded since the location of the checking
            information is made known to blockade() function only during
            linking.
    
         /uf=USER_FILENAME
    
            Before branding, read the file USER_FILENAME and place the 
            contents of the file into the user space reserved when you 
            ran MKSIG.  This is the preferred method since both 
            printable and binary chars may be inserted.
            This switch and the /us switch may not be used together.
         
         /us=STRING
    
            Before branding, insert "STRING" into the user space 
            reserved when you ran MKSIG.  Note that there can be no 
            spaces in STRING (sorry, the arg parser doesn't allow it).
            This switch and the /uf switch may not be used together.
         
         /s=signature_string (optional)
    
            Specifies the character string to look for. This string
            must occur only once in your executable program.
            The signature IS case sensitive.
            The default string is "chk_signature". It must match the
            string embedded in SIGNATUR.H.
    













             Blockade, (C) Copyright 1991-92 Indusoft Corp.  page -11-


         
         
         BRAND.EXE (cont.)
    
    
         /n   (optional)
    
           Tells Brand not to verify the check value immediately after
           it is calculated.  Using this option speeds the BRAND process
           by  about 40%.  I recommend you use it once you feel
           comfortable with BRAND's operation.
    
         
         /c=function  (optional, full version only)
    
           Specifies that BRAND use 1 of 3 (currently) available self
           checking algorithms to brand the program.  The full version
           of BLOCKADE allows you to specify at link time the algorithm
           you desire to use. The specification handed to BRAND via
           this switch must match that used in your program, else your
           blockade() function will think your executable has been
           altered.
    
          Brand will terminate with the following error levels if an error 
          occurs.
               1 = brand's own BLOCKADE() call returned an error.
               2 = some notable but not fatal logic error
                   or illogical data was passed to it.
               3 = a severe error. Your program was probably not
                   branded properly. 



























             Blockade, (C) Copyright 1991-92 Indusoft Corp.  page -12-


    
    
          SUPPORT
    
          Indusoft Corp. can be contacted as follows:
    
          Phone:  (803)-292-9066.
                  Please leave name, phone (including area code),
                  and times when you can be reached.
                  Sorry, I must call COLLECT.
    
          Compuserve ID:  73517,1107
                  I check for mail every couple of days.
                  This is the preferred method.
    
          Prodigy ID:  GHVR03A
                  I check for mail every couple of days.
    
    
    
         TERMS OF USE
    
         BLOCKADE is supplied for personal, private use.  Feel free to
         distribute the non-registered version of BLOCKADE given these
         restrictions:
    
         -  The program shall be supplied in its original, unmodified
            form, which includes this documentation.
    
         -  No fee is charged other than media materials.
    
         -  Commercial use without a license is prohibited.
    
         -  No component of this package may be included, or bundled
            with other  goods or services.  Exceptions may be granted
            upon written request only.  This restriction also applies
            to distributors, and shareware outlets.




















             Blockade, (C) Copyright 1991-92 Indusoft Corp.  page -13-


    
    
         WARRANTY
    
         This program is provided AS IS without any warranty, expressed
         or implied, including but not limited to the program's
         suitability for any specific purpose.  Considerable testing
         effort has been expended in BLOCKADE's development, but the
         user is responsible for determining the program's suitability
         for use.  The user assumes full risk as to the results of using
         this package.  In no event shall Indusoft be liable for any
         consequential damages arising from the use, or inability to use
         these routines.
    
         The idea of shareware with its low cost distribution of quality
         programs can be of great value to computer users.  BLOCKADE
         follows in that tradition.
    
                          THANK YOU FOR YOUR SUPPORT!
    
    
    
    
         -------------------- REGISTRATION BENEFITS ------------------------
    
    
         Registration allows Indusoft to continue improving BLOCKADE and
         to develop new products for the computing community.  Future
         improvements for BLOCKADE include..
    
         *  Adding serial numbers or other data after linking. This will
            allow you to have a plain vanilla EXE file which you customize
            prior to shipment.  (COMPLETED).
    
         *  The ability to embed codes for multiple files, allowing a
            master program to check both itself and subordinates.
    
         *  Ideas that you, our customers submit.
    
         Blockade registration only comes in 2 versions, described below:
    
         License to use the current and all future
         shareware versions for private use ...................... $ 10
    
         License for business and commercial use,
         (includes full source code and license to
          embed object code in your product)  .................... $ 30
    
    
         Please make checks or money orders payable to:
    
                         Indusoft Corp.
                         PO Box 26747
                      Greenville, SC  29616-1747



             Blockade, (C) Copyright 1991-92 Indusoft Corp.  page -14-


    
    
                       REGISTRATION - ORDER FORM
                      ============================
    
    
    
         Please Register BLOCKADE as follows:
    
    
                      Shareware version  ($10.00)   ______
    
                      Commercial version ($30.00)   ______
    
    
         Send applicable material to:
    
         Name: ___________________________________  Phone:_____________
    
         Company: _____________________________________________________
    
         Address: _____________________________________________________
    
         Address: _____________________________________________________
    
         City, State, Zip: ____________________________________________
    
    
         Please specify compiler & version you are using:
         
         Turbo C _____  Turbo/Borland C++ _____   Microsoft C _____
         
    
         Where did you learn about our program?
    
         ______________________________________________________________
    
         What products are you using BLOCKADE for?
    
         ______________________________________________________________
    
         How can we improve BLOCKADE?
    
         ______________________________________________________________
    
         ______________________________________________________________
    
         ______________________________________________________________
    
    
         Please forward check or money order payable to:
    
                          Indusoft Corp.
                          PO Box  26747
                       Greenville, SC  29616-1747
    

             Blockade, (C) Copyright 1991-92 Indusoft Corp.  page -15-


    
























































             Blockade, (C) Copyright 1991-92 Indusoft Corp.  page -16-