JOYSTICK.ZIP                                                Wed  01-08-1992


                       C Game Adapter Library

                             Rev 1.2

                                by

                           Ed Torgerson

                          CIS     70313,456
                          GEnie   E.TORGERSON1.
                          BIX     etorgerson


        A mixed language C and Assembler library of routines for
        accessing the IBM PC game adapter at port 201h.
        Object-Ready, Event-ready design featuring inter-module
        data hiding. (should be easy to change it to a C++ class)

        The low level module is mostly asm statements, but the
        provided small model library module should allow anyone
        with TURBOC 2.0, TURBO C++, or Borland C++ to use it,
        with or without an assembler.  If you need a straight
        C replacement for my low level routines, look at JOY.ARC
        in the Borland C Forum in BPROGB on Compuserve.

        Pseudocode/Structured English modules are also included
        to aid in adapting to other languages.

/*-------------------------------------------------------------------*/

   Files:
       joystklo.c      low level generic game adapter port routines
       joystkmd.c      joystick-specific middle level functions
                           built on top of joystklo.c
       joystick.h      header file for joystklo.c, joystkmd.c
                           and joystk_m.lib
       joystk_s.lib    an already compiled small model library
                           consisting of joystklo.c and joystkmd.c
       testlow.c       a small demonstration of joystklo.c
       testmid.c       a small demonstration of joystkmd.c
       joystklo.se     pseudocode/structured english
       joystkmd.se     pseudocode/structured english

/*-------------------------------------------------------------------*/

    JOYSTKLO.C provides generic low level game-adapter port functions to:

               1.  detect the presence of a game adapter
               2.  verify which axes are functional
               3.  read current button status
               4.  read changed button status
               5.  read current resistive axis position
               6.  allow change of active axes within this system
                   as long as they have been found functional.


   JOYSTKMD.C provides middle level joystick-specific functions to:

               1.  detect and initialize a joystick coordinate system.
               2.  read changed joystick position
               3.  provide a rough translation from the top-left origin
                   joystick coordinate system to a balanced 0,0
                   centered cartesian system
               4.  get/reset joystick center coords
               5.  get/reset joystick minimum coords
               6.  get/reset joystick maximum coords
               7.  get/set an ignore threshold (tolerance) for
                   reading changed joystick positions

/*-------------------------------------------------------------------*/

Background:      

        What I wanted was a decent usable library of functions
    that did a little more than just read the raw port input.
    I don't really use the adapter port that much, but I like
    to cover my bases when it comes to my library.  I've tried
    to make it fairly simple, but fairly versatile.

        The low level module is not joystick specific, so you
    should be able to use it with any other periferal that uses
    the game adapter.  It's coded with assembly statements to make
    the loops a little faster which should be more useful inside
    timer interrupt 1Ch. I didn't really try too hard to optimize
    it, so you should be able to throw it into pure assembly and
    knock a couple of cycles off of it fairly easily.

        I did try to make the middle level module flexible enough
    to use a joystick as a practical pointing device in either a
    polled or an event-driven architecture.  You may want to
    change the ignore threshold system that I've set up to
    compensate for the non-linear scaling of the joystick.  You
    may also want to take a look at my cartesian coordinate
    system.  I've set it up for a center-oriented scale.  Although
    I can't imagine why you might want a different orientation,
    I don't claim to be omniscient, so the translation is performed
    by a seperate function.  If your preference differs from mine,
    you can easily just plug in your own function.

        I've done limited testing on an old IBM XT 5160 model 267
    with 11/08/82 BIOS as well as my PS/2 like 386 AT and haven't
    found anything, yet..........................................

    If you find this library useful, donate to your favorite cause.

    I just want to thank Gary Blaine for putting JOY.ARC out here,
    my function for reading position is based on his.

        These modules are hereby released to the public domain
        by Ed Torgerson : CIS 70313,456,  GEnie E.TORGERSON1.

            Any constructive correspondence is welcome.

/*-------------------------------------------------------------------*/

port 201h :

           bit             JOYSTICK                PADDLE
           ---             --------                ------
           7               B  button 2             D button
           6               B  button 1             C button
           5               A  button 2             B button
           4               A  button 1             A button
           3               B  y-axis               D Coordinate
           2               B  x-axis               C Coordinate
           1               A  y-axis               B Coordinate
           0               A  x-axis               A Coordinate

/*-------------------------------------------------------------------*/
/*--------------------- Low Level Functions -------------------------*/
/*-------------------------------------------------------------------*/
                    
JstDetect :

    purpose:    Detect active game port axes.

    syntax:     int  JstDetect ( void ) ;

    remarks:    performs check by reading port 201h, triggering the
                one-shot timers and immediately checking for bits
                that have changed.  It also sets up valid and
                active axes.

    returns:    bit mask of valid axes in original port format.
                values can be easily checked by ANDing this value
                with the defined macros:

                            JOYSTICK_A, JOYSTICK_B
                    JAX_AXIS, JAY_AXIS, JBX_AXIS, JBY_AXIS
          
/*-------------------------------------------------------------------*/

JstGetButton :

    purpose:    returns the current button value.

    syntax:     int  JstGetButton ( void ) ;

    remarks:    This is not just a straight read of port 201h.
                It is intended to provide quick determination
                of the current status using macros.

    returns:    bit mask of current button state.
                values can be easily checked by ANDing this
                value with the defined macros:

           JA1_BUTTON_DOWN, JA1_BUTTON_UP,
           JA2_BUTTON_DOWN, JA2_BUTTON_UP
           JB1_BUTTON_DOWN, JB1_BUTTON_UP,
           JB2_BUTTON_DOWN, JB2_BUTTON_UP
           J_ANY_BUTTON_DOWN
           J_A_BUTTON_DOWN, J_B_BUTTON_DOWN
           J_BUTTON_1_DOWN, J_BUTTON_2_DOWN

           bit      STATE        JOYSTICK           PADDLE
           ---      -----        --------           ------
           7        down         B  button 2        D button
           6        down         B  button 1        C button
           5        down         A  button 2        B button
           4        down         A  button 1        A button
           3         up          B  button 2        D button
           2         up          B  button 1        C button
           1         up          A  button 2        B button
           0         up          A  button 1        A button

/*-------------------------------------------------------------------*/

JstGetChangedButton

    purpose:    returns any change in button state since
                the last call to either JstGetChangedButton
                or JstGetButton.

    syntax:     int  JstGetChangedButton( void ) ;

    remarks:    see JstGetButton

    returns:    see JstGetButton

/*-------------------------------------------------------------------*/

JstGetPosition  :

    purpose:    returns the position of the given axis.

    syntax:     int  JstGetPosition ( int axis ) ;

    remarks:    'axis' is a bit mask of a single active axis
                in original port format and may be specified
                with one of the following defined macros:

                    JAX_AXIS, JAY_AXIS, JBX_AXIS, JBY_AXIS

    returns:    the position of the given axis in the original
                coordinate system.  The values for a 100k
                joystick should be between 4 and 400, but may
                exceed these limits, especially with the
                adjustment sliders on most joysticks.

/*-------------------------------------------------------------------*/

JstGetValidAxes

    purpose:    returns a bit mask of the valid axes found by
                JstDetect() in original port format.

    syntax:     int  JstGetValidAxes ( void ) ;

    remarks:    intended to be use before an attempt to set the
                current active axis mask with JstSetActiveAxes().

    returns:    bit mask of valid axes in original port format.
                Values can be easily checked by ANDing this value
                with the defined macros:

                            JOYSTICK_A, JOYSTICK_B
                    JAX_AXIS, JAY_AXIS, JBX_AXIS, JBY_AXIS
    
/*-------------------------------------------------------------------*/

JstGetActiveAxes

    purpose:    returns a bit mask of the currently active axes
                used in error checking by JstGetPosition() in
                original port format.

    syntax:     int  JstGetActiveAxes ( void ) ;

    remarks:    This mask is used to screen out possible calls
                to time axes that may be valid, but are not
                in use, thus saving precious cycles.

    returns:    bit mask of currently active axes in original port
                format. Values can be easily checked by ANDing this
                value with the defined macros:

                            JOYSTICK_A, JOYSTICK_B
                    JAX_AXIS, JAY_AXIS, JBX_AXIS, JBY_AXIS
    

/*-------------------------------------------------------------------*/

JstSetActiveAxes

    purpose:    sets valid axes for read operations by
                JstGetPosition().

    syntax:     int  JstSetActiveAxes ( unsigned mask ) ;

    remarks:    The value is written only if the entire given
                mask is valid.  Validity may be determined
                beforehand by getting a mask of valid axes
                with JstGetValidAxes().

    returns:    1 on success, 0 if mask is invalid.

/*-------------------------------------------------------------------*/
/*------------------- Middle Level Functions ------------------------*/
/*-------------------------------------------------------------------*/

JstInitialize
                                                 
    purpose:    to detect and initialize joysticks

    syntax:     int  JstInitialize ( void (*NotifyUserFunc)(int) ) ;

    remarks:    This function first calls JstDetect to determine
                if a joystick(s) is installed and set up valid and
                active joystick axis pairs.  It then calls the
                given user notification function NotifyUserFunc()
                to prompt the user to enter the center, minimum,
                and maximum joystick coordinate pairs.  At any
                point during the user data input step, the user
                may quit the process by pressing escape.  This
                function then calculates the starting ignore
                threshold (tolerance) and quasi linear scale for
                calls to JstGetChangedPosition().

                NotifyUserFunc is a pointer to a user provided
                function which prompts the user for input during
                the intialization process.  It takes one parameter,
                an integer to determine what message to display.
                The function's format should be as follows...

        void NotifyUserFunc( int msg )
        BEGIN
        switch (msg)
            case  -2: "warning: joystick installation incomplete"
            case  -1: "joystick installation terminated by user"
            case   0: "no joystick detected"
            case   1: "press escape to quit"
            case   2: "center joystick and press button"
            case   3: "move joystick to top-left and press button 1"
            case   4: "move joystick to lower-right and press button 2"
            case  -3: return
            default : return
        END

    returns:    1 on success, 0 on failure

/*-------------------------------------------------------------------*/

JstGetChangedPosition

    purpose:    return position of given joystick if it has
                changed past the tolerance scale (ignore threshold).

    syntax:     int JstGetChangedPosition ( int stick,
                                struct JoystickPosition *stickpos ) ;

    remarks:    the tolerance scale is set to decrease from
                the maximum value as set by JstSetTolerance()
                and JstInitialize() at the bottom-right corner
                of the joystick through three asymetric steps
                set towards the upper-left corner.  This scale
                is intended to produces a more linear action
                across the span of the joystick with a minimum
                of calculation (time).

                The value of 'stick' may be easily set with the
                defined macros JOYSTICK_A and JOYSTICK_B. The
                joystick position (if changed) is returned in
                the JoystickPosition structure 'stickpos'.
                The values in stickpos are undefined if the
                position has not changed.

    returns:    1 if 'stickpos' contains a new position.
                0 if no change.

/*-------------------------------------------------------------------*/

JstGetTolerance

    purpose:    return maxmimum value on the tolerance scale
                (ignore changed position threshold).

    syntax:     int  JstGetTolerance ( void ) ;

    remarks:    this value is originally set as the combined
                maximum joystick coordinates divided by 64 which
                should generally yield a value around 10.

    returns:    positive integer

/*-------------------------------------------------------------------*/

JstSetTolerance

    purpose:    sets the tolerance value (ignore changed position
                threshold) for the top of the scale at the
                joystick's bottom-right for JstGetChangedPosition()

    syntax:     void JstSetTolerance ( int tolerance ) ;

    remarks:    this value is originally set as the combined
                maximum joystick coordinates divided by 64 which
                should generally yield a value around 10.

    returns:    void

/*-------------------------------------------------------------------*/

JstSetCenter

    purpose:    grabs the current coordinates of the given joystick
                and set the center of the cartesian system to that
                point. It also resets the tolerance scale.

    syntax:     int  JstSetCenter ( int stick ) ;

    remarks:    The value of 'stick' may be easily set with the
                defined macros JOYSTICK_A and JOYSTICK_B. 

    returns:    1 on success, 0 if invalid joystick.

/*-------------------------------------------------------------------*/

JstSetMin

    purpose:    grabs the current coordinates of the given joystick
                and stores it as the minimum joystick position.
                It also resets the tolerance scale.

    syntax:     int  JstSetMin ( int stick ) ;

    remarks:    The value of 'stick' may be easily set with the
                defined macros JOYSTICK_A and JOYSTICK_B. 

    returns:    1 on success, 0 if invalid joystick.

/*-------------------------------------------------------------------*/

JstSetMax

    purpose:    grabs the current coordinates of the given joystick
                and stores it as the maximum joystick position.
                It also resets the tolerance scale.

    syntax:     int  JstSetMax ( int stick ) ;

    remarks:    The value of 'stick' may be easily set with the
                defined macros JOYSTICK_A and JOYSTICK_B.

    returns:    1 on success, 0 if invalid joystick.

/*-------------------------------------------------------------------*/

JstGetCenter

    purpose:    returns the current coordinates of the set
                center position of the given joystick.

    syntax:     void JstGetCenter( int stick,
                                struct JoystickPosition *jpos ) ;

    remarks:    The value of 'stick' may be easily set with the
                defined macros JOYSTICK_A and JOYSTICK_B.

    returns:    void

/*-------------------------------------------------------------------*/

JstGetMin

    purpose:    returns the current coordinates of the set
                minimum position of the given joystick.

    syntax:     void JstGetMin ( int stick,
                                struct JoystickPosition *jpos ) ;

    remarks:    The value of 'stick' may be easily set with the
                defined macros JOYSTICK_A and JOYSTICK_B.

    returns:    void

/*-------------------------------------------------------------------*/

JstGetMax

    purpose:    returns the current coordinates of the set
                center position of the given joystick.

    syntax:     void JstGetMax ( int stick,
                                struct JoystickPosition *jpos ) ;

    remarks:    The value of 'stick' may be easily set with the
                defined macros JOYSTICK_A and JOYSTICK_B.

    returns:    void

/*-------------------------------------------------------------------*/

JstXlatToCart

    purpose:    translate the given coordinates from real to
                cartesian coordinates.

    syntax:     void JstXlatToCart ( int stick,
                                struct JoystickPosition *stickpos ) ;

    remarks:    'stickpos' contains the real coordinates to be
                translated and returns cartesian values based on
                the set center of the joystick 'stick'.

    returns:    void

/*-------------------------------------------------------------------*/

/*-- end joystick.doc */