;------------------
;   CM_INT -- Interrupt Service by CMartin -- 2/22/92
;   Member ASP; CompuServe 72130,1400
;   The Program CM_INT is released as Freeware.  No contribution is expected.
;------------------
;   Intended as a tool kit for 80x86 Assembly Language programmers, this
;   service may also be useful to high level language programmers whose
;   language gives them access to the 80x86 interrupt architecture.
;   This interrupt service installs and stays resident, by including the
;   command cm_int in autoexec.bat, and cm_int.com in root directory, or by
;   running cm_int before any programs that use this interrupt service.
;   The functions in this service preserve the general purpose registers not
;   used for data transfer. They also preserve the segment, index and base
;   pointer registers.
;
;   This service is accessed via Int 0C0h, with function number passed through
;   bh. Description of each function follows:
;------------------
;
;   PAUSE
;       Function 00h: Pause until specific key is pressed.
;           Entry:  bl      - ASCII code of keypress required to
;                            release pause
;                   bh      - 00h
;           Return: None
;------------------
;
;   PRINT
;       Function 01h: Print string at current cursor position.
;           Entry:  ds:si   - pointer to ASCIIZ source string
;                   bh      - 01h
;           Return: None
;------------------
;
;   INPUT
;       Function 02h: Input a string from keyboard at current cursor position
;           Entry:  ds:si   - pointer to destination string
;                   bh      - 02h
;           Return: None
;------------------
;
;   SCAN (INPUT TO SCREEN) WITH PROMPT AND EDIT
;       Function 03h: Scan with prompt and editing at current cursor position
;           Entry:  ds:si   - pointer to ASCIIZ prompt string
;                   ds:di   - pointer to ASCIIZ destination string for
;                               data being entered/edited
;                   al      - data length - desired length of entry string
;                   ah      - data type -   0:no filtering
;                                           1:filter non-printable
;                                           2:numbers (0-9),blanks,and '+-'
;                                           3:numbers,blanks,and 'eE+-'
;                                           4:dates (0-9,'/-' and blank)
;                   bl      - 0=upper and lower case, >0=lower converted to
;                                  upper
;                   cl      - blank option- 0:no stripping
;                                           1:strip leading blanks
;                                           2:strip trailing blanks
;                                           3:strip both leading and trailing
;                   ch      - data window color (prompt field color is same
;                               backgnd as orig scrn attr, with hi intensity
;                               white foregnd. On exit, orig scrn attr are
;                               restored in all fields)
;                   bl      - 0:Upper and lower case; >0:Converts to upper
;                   bh      - 03h
;           Return: bl      - ASCII char code describing which keypress
;                               terminated data entry. A number of termination
;                               key combinations with corresponding codes are
;                               built in for versatility, and are all
;                               available. The returned byte ASCII character,
;                               the key combo that produces it, and the
;                               suggested usage follows:
;
;           'I'-<Ctrl><Rtn> {In}        'O'-<Ctrl><F10>-Delete block {Out}
;           'D'-Down arrow              'U'-Up arrow
;           'A'-<PgUp>                  'Z'-<PgDn>
;           'N'-<Ctrl>N-Insert New line 'Y'-<Ctrl>Y-Delete line
;           'L'-<Ctrl>L-Move Col Left   'R'-<Ctrl>R-Move Column Right
;           'C'-<Rtn> {Carriage}        'E'-<Esc>
;           'X'-Error - prompt plus data > 4 lines or off bottom of screen
;------------------
;
;   LINE PRINT
;       Function 04h: Print to parallel port printer
;           Entry:  ds:si   - pointer to string to be printed
;                   cx      - -1 means string is ASCIIZ and is to be printed
;                                   up to the terminal NULL
;                             Number other than -1 means print that number of
;                                   characters. (Permits 0 as a print control
;                                   character.)
;                   bh      - 04h
;           Returns: If print terminated by <Esc>, then leaves keypress in
;                             keyboard buffer, accessible by int 16h, func 1
;------------------
;
;   32-BIT NUMBER TO ASCIIZ
;       Function 06h: 32-bit binary number to ASCIIZ string
;           Entry:  dx:ax   - 32-bit signed binary number to be converted
;                   ds:si   - pointer to ASCIIZ destination string
;                   bl      - format for string:
;                               0=decimal,1=hex,2=octal,3=binary
;                   bh      - 03h
;           Returns: None
;------------------
;
;   ASCIIZ TO 32-BIT NUMBER
;       Function 07h: ASCIIZ string to 32-bit signed number
;           Operation:  Function scans from rightmost byte in string until
;                           beginning of field, ignoring illegal characters.
;                           Terminal h or H means hex;o or O octal; b or B bin
;           Entry:  ds:si   - pointer to ASCIIZ source string
;                   bh      - 04h
;           Returns: dx:ax  - 32-bit signed binary number  (0:0 for overflow)
;                    bl = 0 (normal return), -1 (overflow)
;------------------
;
;   JULIAN TO CALENDAR DATE
;       Function 10h: Convert julian date to calendar date.
;           Operation: Julian date is sent in on ax as unsigned 16-bit
;               binary number, where julian date 1=calendar date 1/1/1901.
;               Julian date <1 or >36525 (earlier that 1/1/1901 or later
;               that 12/31/2000 [12/31/00]) are illegal
;               Normalized calendar date (mm/dd/yy) is copied as ASCIIZ
;               string at the pointer provide by ds:si. If julian date
;               is in illegal range, the string '  /  /  ' is copied.
;               In addition, the day of the week is returned as a number
;               0-7 through bh (0=illegal,1=Sunday,etc.).The century
;               prefix (e.g., 19 for 1956) is passed through bl.
;           Entry:  bl      - century prefix
;                               (e.g., 19 is century prefix for 1978)
;                   ax      - julian date (unsigned 16-bit) (1=01/01/01)
;                   cx      - number of digits to display year (2 or 4),
;                               if century prefix is 19.
;                               (If century prefix not 19, 4 digits will be
;                               displayed, regardless of contents of cx)
;                   ds:si   - pointer to ASCIIZ destination string where
;                               calendar date is to be copied (11 bytes min)
;                   bh      - 10h
;           Return: ax      - julian date as unsigned 16-bit number
;                               (0 if illegal)
;                   bl      - century prefix
;                   bh      - day of week (0=illegal,1=Sunday,etc.)
;                   cx      - year (1980-2099)   (as expected by system set
;                   dh      - month (1-12)       date service int 21h, 2Bh)
;                   dl      - day (1-31)
;------------------
;
;   CALENDAR TO JULIAN DATE
;       Function 11h: Convert calendar date to julian date
;           Operation: Converse of Function 10h, except that calendar
;               date string is normalized to 9-byte or 11-byte ASCIIZ form
;               (mm/dd/yy+terminal NULL or mm/dd/yyyy+NULL, depending on
;               whether year was 2 or 4 bytes to begin with). If year was
;               passed in as 2 bytes, default century prefix is 19.
;               '  /  /  ' is copied to the  string if format is illegal.
;           Entry:  ds:si   - pointer to ASCIIZ source string (11 bytes min)
;                   bh      - 11h
;           Return: Same as Function 10h
;------------------
;
;   GET SYSTEM DATE
;       Function 12h: Get today's date from system and convert
;               to julian and calendar date
;           Entry:  ds:si   - pointer to destination string for cal date
;                   cx      - number of digits to display year (2 or 4),
;                               if century prefix is 19.
;                               (If not 19, 4 digits will be shown.)
;                   bh      - 12h
;           Return: Same as Function 10h
;------------------
;
;   SET SYSTEM DATE
;       Function 13h: Set date in system from ASCIIZ string
;           Entry:  ds:si   - pointer to source string of form mm/dd/yy or
;                               mm/dd/yyyy
;                   bh      - 13h
;           Return: Same as Function 10h
;------------------
;
;   TIME (SECONDS) TO ASCIIZ STRING
;       Function 15h: Convert time in seconds to string
;           Entry:  ds:si   - pointer to destination string for time
;                               Will be normalized to form hh:mm:ss
;                   dx:ax   - double word number of seconds since midnite
;                   bh      - 15h
;           Return: dx:ax   - double word number of seconds since midnite
;                   ch      - hours
;                   cl      - minutes
;                   bh      - seconds (similar to DOS get time utility,
;                   bl      - 0         except seconds:100ths in bx)
;------------------
;
;   ASCIIZ STRING TO TIME (SECONDS)
;       Function 16h: Convert string time to time in seconds
;                       Procedure normalizes string time to form hh:mm:ss
;           Entry:  ds:si   - pointer to source string for time
;                   bh      - 16h
;           Return: Same as Function 15h
;------------------
;
;   GET SYSTEM TIME
;       Function 17h: Get system time and convert to string and seconds
;           Entry:  ds:si   - destination string pointer
;                   bh      - 17h
;           Return: Same as Function 15h
;------------------
;
;   SET SYSTEM TIME
;       Function 18h: Set system time from ASCIIZ string
;           Entry:  ds:si   - source string pointer (hh:mm:ss)
;                   bh      - 18h
;           Return: Same as Function 15h
;------------------
;
;   TIMER
;       Function 19h: Elapsed time timer
;           Entry:  bh      - 19h
;           Return: dx:ax   - Elapsed seconds since previous midnight
;                   bx      - Elapsed seconds since last call to timer
;------------------
;
;   ASCIIZ STRING COPY
;       Function 20h: String copy to NULL
;           Entry:  ds:si   - source string pointer
;                   ds:di   - destination string pointer
;                   bh      - 20h
;           Return: None
;------------------
;
;   ASCIIZ STRING LENGTH
;       Function 21h: String length
;           Entry:  ds:si   - source string pointer
;                   bh      - 21h
;           Return: ax      - string length
;------------------
;
;   ASCIIZ STRING CONCATENATE
;       Function 22h: String concatenate
;           Entry:  ds:di   - pointer to string to which source string is
;                               to be added
;                   ds:si   - pointer to source string to be concatenated
;                               to ds:di
;                   bh      - 22h
;           Return: None
;------------------
;
;   ASCIIZ STRING COMPARE
;       Function 23h: String compare
;           Entry:  ds:si   - pointer to string 1
;                   ds:di   - pointer to string 2
;                   cx      - max number of bytes to compare
;                   bh      - 23h
;           Return: ax      - 1 if str1>str2, 0 if str1=str2, -1 if str1<str2
;                   bx      - unsigned number = position of differing byte
;------------------
;
;   ASCIIZ STRING SWAP
;       Function 24h: String swap
;           Entry:  ds:si   - pointer to string 1
;                   ds:di   - pointer to string 2
;                   cx      - string length
;                   bh      - 24h
;           Return: None
;------------------
;
;   ASCIIZ STRING IMBED
;       Function 25h: String imbed - Imbeds source string at destination
;               offset, but does not copy terminal NULL. Good for implanting
;               ASCII data into a print line.
;           Entry:  ds:si   - pointer to source string
;                   ds:di   - pointer to imbed destination
;                   bh      - 25h
;           Return: None
;------------------
;
;   ASCIIZ STRING ALL CAPS
;       Function 26h: All caps - Capitalizes all lower case letters in the
;               ASCIIZ string pointed to by ds:si; max of cx characters
;           Entry:  ds:si   - pointer to string to be capitalized
;                   cx      - maximum number of chars to capitalize
;                   bh      - 26h
;           Return: None
;------------------