CLOCK

CLOCK.SYS is a clock device driver (CLOCK$ device).  It replaces the DOS 
internal clock driver for those whose clocks are not supported by the level
of DOS they are using or want to use.  CLOCK supports a wide variety of 
different clock hardware and BIOS interfaces.  As far as possible, CLOCK will
automatically determine what clock interface to use.  If the automatic 
determination does not work for your system, you may tell CLOCK specifically
what interface type to use.

If your PC clock is not currently supported but you would like to remove the
restrictions on what versions of DOS you can use, please contact me by mail or
on CompuServe.  I will be happy to add support for your clock.  I will need
some technical information and help from you in getting it to work so I will
give you a $0 usage license for your help.  Likewise, anyone finding a new bug
and helping me get the information to correct it will get a $0 usage license.

DEFINITION OF SHAREWARE

Shareware distribution gives users a chance to try software before buying
it. If you try a Shareware program and continue using it, you are expected
to register. Individual programs differ on details -- some request
registration while others require it, some specify a maximum trial period.
With registration, you get anything from the simple right to continue using
the software to an updated program with printed manual.

Copyright laws apply to both Shareware and commercial software, and the
copyright holder retains all rights, with a few specific exceptions as
stated below. Shareware authors are accomplished programmers, just like
commercial authors, and the programs are of comparable quality. (In both
cases, there are good programs and bad ones!) The main difference is in the
method of distribution. The author specifically grants the right to copy
and distribute the software, either to all and sundry or to a specific
group. For example, some authors require written permission before a
commercial disk vendor may copy their Shareware.

Shareware is a distribution method, not a type of software. You should find
software that suits your needs and pocketbook, whether it's commercial or
Shareware. The Shareware system makes fitting your needs easier, because
you can try before you buy. And because the overhead is low, prices are low
also. Shareware has the ultimate money-back guarantee -- if you don't use
the product, you don't pay for it.

DISCLAIMER - AGREEMENT

Users of CLOCK must accept this disclaimer of warranty:  "CLOCK is
supplied as is.  The author disclaims all warranties, expressed or implied,
including, without limitation, the warranties of merchantability and of
fitness for any purpose.  The author assumes no liability for damages,
direct or consequential, which may result from the use of CLOCK."

CLOCK is a "shareware program" and is provided at no charge to the user
for evaluation.  Feel free to share it with your friends, but please do not
give it away altered or as part of another system.  The essence of
"user-supported" software is to provide personal computer users with
quality software without high prices, and yet to provide incentive for
programmers to continue to develop new products.  If you find this program
useful and find that you are using CLOCK and continue to use CLOCK after
a reasonable trial period, you must make a registration payment of $10 to
Ronald Q. Smith.  The $10 registration fee will license one copy for use on
any one computer at any one time.  For a registration fee of $25, I will
immediately send you the latest version of CLOCK including the source
code.  You may use the source code for your own maintenance of CLOCK or as
a learning tool for any software that you develop.  You may not use all or
part of the source code in any software that you develop or release to
others without the permission of Ronald Q. Smith.

You must treat this software just like a book.  An example is that this
software may be used by any number of people and may be freely moved from
one computer location to another, so long as there is no possibility of it
being used at one location while it's being used at another.  Just as a
book cannot be read by two different persons at the same time.

Commercial users of CLOCK must register and pay for their copies of CLOCK
within 30 days of first use or their license is withdrawn.  Site-License
arrangements may be made by contacting Ronald Q. Smith.

Anyone distributing CLOCK for any kind of remuneration must first contact
Ronald Q. Smith at the address below for authorization.

You are encouraged to pass a copy of CLOCK along to your friends for
evaluation.  Please encourage them to register their copy if they find that
they can use it.  All registered users will receive a copy of the latest
version of the CLOCK system.

Send the fees and any inquiries to:

                        Ronald Q. Smith
                        11 Black Oak Road
                        North Oaks, Mn. 55127-6204

You may also contact me via CompuServ mail at userid 71620,514.  I will be
happy to respond to any problems and suggestions for future capabilities.

USING CLOCK

To install the device driver include the following line in CONFIG.SYS:

DEVICE=[d:][path\]CLOCK.SYS [type][,io_addr]
               or
DEVICE=[d:][path\]CLOCK.SYS 3[,segment[,write0,write1,read]]
               or
DEVICE=[d:][path\]CLOCK.SYS A[,base_year]

where "d:" and "path\" identify the drive and directory containing CLOCK.SYS.

"type" allows you to control which clock interface will be used.  It may be
important if the automatic determination does not work on your system.  
See the information below for some help in determining the type number for 
your system.

If "type" is an I/O clock (types 4, 6, 7, and 9), you may add "io_addr" to 
specify the I/O address used by your clock.  Normally this is 240, 2C0, or 340
for types 4, 6, and 7 and 210 or 310 for type 9.  All numbers are in hex.  For 
example, an AST Research clock might be specified as follows:

DEVICE=[d:][path\]CLOCK.SYS 4,2C0

If you do not specify the "io_addr", CLOCK.SYS will try to determine the 
correct address by probing.

If you are sure that you have an I/O clock but you are not sure which one it
is, specify type 8 and supply the io_addr if possible.  Type 8 does not
represent a specific clock.  Rather it attempts to determine whether your
clock is a type 4, 6, 7, 9, or B using a sequence of operations also used by 
some of the I/O clock vendors.

If you have a memory mapped clock, you may use the second format to specify 
the addresses to be used.

"segment" is the base address used to access the clock.  Usually your 
documentation will give the segment address as four hex digits such as FE00 or
F000.  Some addresses may be less than four digits (e.g., 70).  Other 
documentation may show addresses in the form xxxx:yyyy.  In this case the
segment address is the xxxx value.

"write0" is the offset used to write 0 bits.  It must also be a hex address and
may be 0, F002, or anything else the vendor chose.  If the addresses are
given in the xxxx:yyyy form, use the yyyy.

"write1" is the offset used to write 1 bits.

"read" is the offset used to read bits.

If your documentation gives the segment address but isn't clear about the
offsets, just specify the segment address and CLOCK.SYS will try all offset
combinations that it knows about.

If you specify one of the offsets, you must specify them all.

"base_year" is used for the AT&T 6300 clocks (type=A).  Dates prior to that
year or more than 7 years after that year will not be handled correctly.  If
no base year is specified 1992 will be used.  Dates between the start of the
base year and the end of the seventh year later are handled (e.g., 1992-1-1
until 1999-12-31).

All DOS DATE and TIME commands and all DOS date and time function calls
will use the calendar clock as they did in earlier DOS versions released by 
the vendor.

CLOCK.SYS supports all valid DOS dates from 1-1-1980 to 12-31-2079 and
handles leap years automatically.

CLOCK TYPE

There are almost as many different implementations of PC clocks as there are
different types of PCs.  Until the PC/AT came along, there was no standard for
battery protected clocks and each PC and add-in was likely to implement them
differently.  With the PC/AT a standard and documented interface for such
clocks was provided.  Since that time, most PCs have followed the PC/AT
standard.  It is earlier PCs, especially 8088 PCs, that don't follow the
standard.  Since these are early PCs, there is also a high probability that 
the vendor is no longer providing modified versions of DOS with built-in
support for their clocks.  This leaves you faced with the choice between 
staying with DOS 3.2 or earlier or giving up your clock.

CLOCK.SYS is intended to free you from those limitations.  It will work with
all versions of DOS from 2.10 through 5.00 and undoubtedly beyond.  It also
attempts to automatically determine what kind of clock you have and install
the correct support for it.  However, there are often enough differences 
between PCs that the automatic determination will not find anything or will
even make the wrong choice.  To give you more control of the situation, you
may specify the clock interface by giving an interface number.

It will not always be easy to decide what interface number to use.  You will
at least need some technical information on how your clock works or on the
BIOS calls used to control the battery-protected clock.  If you find a 
description below that seems to match, give it a try.  The most that should go
wrong is that your time and date will be set incorrectly, but then they 
probably weren't working anyhow.

If you aren't sure what interface to use or if you are sure that your clock is
not supported, LET ME KNOW.  I WOULD LIKE TO HELP.  You can help me make 
CLOCK.SYS better for everyone.  I would even like to here from you if CLOCK.SYS
did work for you.  I would like to be able to add your PC manufacturer and 
model number to the supported list so others know what to use.  If CLOCK.SYS 
did not work for you, I am interested in making the changes so that it does 
work.  If you can provide me with the necessary technical information, I will 
make the changes.

Usually, a technical reference manual with hardware and BIOS interfaces is the
best source.  Even if you don't have one, your original hardware vendor may be
willing to send you enough information to allow you to program the clock.  If
all else fails, we may even be able to use an old copy of DOS or a clock 
setting utility to figure out how it works.  Before we do that, check your
license to be sure that it is not forbidden to disassemble the software to see
how the clock works.  

The following table shows the systems that have been determined to work with
existing clock types.  If your system is in the list, try the clock type
indicated.  If not, look through the next table which tells you about the
characteristics of each type of clock and see if anything seems to match
your system type.

SYSTEM                  CLOCK TYPE
------                  ----------
Amstrad PC1521DD        0
AST Research            8 (4, 6, 7) See discussion under clock types
  Six-Pack
  I/O Plus, etc.
AT&T 6300               A
Hyundai 8088            B
IBM PC/AT               0
Leading Edge Model D    5
Mitsubishi 8088         5
Quadram Corp            9
  QuadCard
  QuadCard II
  QuadCard 512+
SMT No-Slot Clock       3
Sperry PC-1             5
Sperry PC/HT            5
Tandy 1200HD            4
Vendex Turbo-888-XT     4
Zenith Supersport 20    1
Zenith Z-18x            1



TYPE                INTERFACE DESCRIPTION AND PCs THAT USE THIS TYPE

 0              IBM PC/AT and all fully compatible PCs.  Interface 0 is 
                included for completeness.  Most versions of DOS fully support 
                this clock interface without a separate driver.

                Amstrad PC1521DD systems use this type of clock.
                
                Automatic determination checks location F000:FFFE for the hex
                value FC.

                BIOS calls are used to read and write the clock values which
                are usually stored in the CMOS RAM along with other 
                configuration information.  The primary interfaces are:
                
                Get Date:       MOV   AH,4
                                INT   1AH
                                Returns the year in CX and month and day in DX
                                in BCD format (e.g., a hex display would show:
                                CX=1991, DX=1009 for October 9, 1991).

                Set Date:       MOV   AH,5
                                Load CX and DX as above for Get Date
                                INT   1AH

                Get Time:       MOV   AH,2
                                INT   1AH
                                Returns hours and minutes in CX and seconds in
                                DH in BCD format.  May also return 100ths of
                                seconds in DL (e.g., CX=2359, DX=5900 for 1
                                second before midnight).

                Set Time:       MOV   AH,3
                                Load CX and DX as for Get Time
                                INT   1AH
_______________________________________________________________________________
 1              Zenith Z-18x 8088 portables, Zenith Supersport 20.

                Automatic determination checks location F000:FFFA for the two-
                byte hex value 4D32 ("M2").

                BIOS calls are used to read and write the clock

                Get Date:       MOV   AH,2
                                INT   1AH
                                Returns CX=year (1980 - 2079) in binary and
                                DH=month, DL=day.  All values are binary.
                                A hex display of the above date would look
                                like CX=7C7, DX=A09.

                Set Date:       MOV   AH,3
                                Load CX and DX as for Get Date.
                                INT   1AH

                Get Time:       MOV   AH,4
                                INT   1AH
                                Returns CH=hours, CL=minutes, DH=seconds.
                                A hex display would show: CX=173B, DX=3B00.

                Set Time:       MOV   AH,5
                                Load CX and DX as for Get Time.
                                INT   1AH
______________________________________________________________________________
 2              Various Zenith Data System PCs.

                Automatic determination looks at location F000:800A for the
                pattern 00,F0,"ZDS".

                Get Date:       MOV   AH,2AH
                                INT   1AH
                                Returns CX and DX as for type 1.

                Set Date:       MOV   AH,2BH
                                Load CX and DX as for type 1.
                                INT   1AH

                Get Time:       MOV   AH,2CH
                                INT   1AH
                                Returns CX and DX as for type 1.
                                
                Set Time:       MOV   AH,2DH
                                Load CX and DX as for type 1.
                                INT   1AH
______________________________________________________________________________
 3              Memory-mapped clock used on some Zenith Data Systems PCs and
                other similar clocks including many slotless or no-slot 
                clocks.  The SMT (Systems Manufacturing Technology) No-Slot
                clocks are supported.

                Automatic determination is to attempt to read the clock.  If
                values other than all 0FFH or 0 are obtained, this clock
                type is chosen.  All known segments and offsets are tried.

                Several different memory mapping approaches are used and
                many different address possibilities are supported.  In 
                general a segment address in the ROM region (C800H through
                FFFFH) is used.  Offsets from that segment address are used
                to read bits, write zero bits, and write one bits.  
                Documentation may specify those segments and addresses in
                several forms.  For example, segment F000 with offset F002
                is the same as segment FF00 with offset 2.
                
                Each memory reference reads or writes a single bit.  Read
                operations are used for all references with separate offsets
                for reading a bit, writing a zero bit, and writing a one bit.

                Clock segments and addresses currently probed include:

        SEGMENT   WRITE0   WRITE1   READ  DECR  LAST      VENDOR
        F000      F002     F003     F004  0000  F000      (Zenith)
        FE00      2        3        5     0080  C800      SMT
        FE00      0        2        8     0080  C800      SMT

                DECR indicates that the segment has that value subtracted from
                it for another attempt at probing until the value falls below
                LAST.  Note that like the segment address, DECR and LAST are
                both in units of paragraphs (16-bytes).  Thus DECR of 80 is
                equivalent to 800H or 2048 bytes.

                When the addresses used by a memory-mapped clock are determined
                by probing, the segment and read address is displayed.  As the
                read address varies the most it is a good indication of the 
                type of clock found.

                Data is stored in BCD in bytes that you construct by shifting
                in the bits.  The most important data bytes are: 
                0 = Hundredths of seconds, 1 = Seconds, 2=Minutes, 3=hours, 
                5=days, 6=months, 7=years mod 1980.
_______________________________________________________________________________
 4              I/O bus clock used on some PCs.  Many add-in clocks on 
                expansion boards are also accessed similarly.  This clock was 
                used on many AST Research I/O boards for 8088 PCs such as the 
                Six-Pack Plus, IO Plus, etc.  Also used on some Tandy systems 
                (e.g., 1200HD) and the Vendex Turbo-888-XT.

                Automatic determination is to attempt to read, complement,
                write, re-read, and re-complement one of the registers.  If the
                first value read and the re-complemented second value are 
                equal, the register exists and is presumed to be the clock.  
                See also the description for types 6 and 7.  If you aren't sure 
                which variant you have, specify type 8 and automatic probing 
                will determine if it is really a type 4, 6, or 7.  For the 
                greatest chance of detecting the correct clock type, supply the
                base I/O address if at all possible.

                NOTE:  If the clock is not correctly initialized (e.g., you
                have just replaced the battery), CLOCK.SYS must initialize it 
                so that the counters will start working.  CLOCK.SYS determines 
                that the clock has been previously initialized by looking at 
                register 14H (see 2D4H below).  If register 14H contains the 
                value 0DEH, the clock is presumed to be initialized.  If not, 
                CLOCK.SYS will clear all the registers to zero and start the 
                counters running.  While this form of checking for initial-
                ization was commonly used, your previous software may have used 
                a different method.  If so, the first time you run CLOCK.SYS 
                your date and time may be set to zero (1980-1-1 00:00:00).  If 
                that happens, just enter the date and time.  It should work OK 
                after that without resetting to zero on further boots.

                Each clock register is implemented as a separate I/O register
                address.  Clock base I/O addresses of 240H, 2C0H, 300H, and 
                340H are supported by automatic probing.  Similar clocks at 
                other base I/O addresses are supported by specifying type 4 and 
                the base address. The address range used is the base plus 0 
                through 1FH (e.g., 2C0H through 2DFH).
                
                Important registers are (using 2C0 as the example):
                
                    2C1  =  100ths of seconds 
                    2C2  =  seconds 
                    2C3  =  minutes 
                    2C4  =  hours 
                    2C6  =  days
                    2C7  =  months
                    2C9  =  month last time clock was read/set 
                    2CA  =  years
                    2CB  =  initialized flag (0DEH if initialized)
                    2D4  =  Status
                    
                All values are in BCD.  That means that each register consists
                of two 4-bit nybbles.  Each nybble contains one decimal digit
                of the value.  Years are mod 1980 (i.e., 0 means 1980, 99 means 
                2079).

                Since these clocks do not keep the year and do not handle leap
                years for you, CLOCK.SYS does the necessary calculations to 
                keep the year correctly maintained and to adjust the date for
                leap days.  The clocks do provide a couple of memory locations 
                in which CLOCK.SYS maintains the year and previous month.  As 
                long as you boot your system before a full year has passed, 
                CLOCK.SYS will correctly maintain the date.
_______________________________________________________________________________
 5              Mitsubishi 8088 PCs.  These were sold by Sperry as the PC-1
                and PC/HT, by Leading Edge as the Model D, by Mitsubishi, and
                others.

                Automatic determination checks location F000:FFB3 for the 
                string "MITSUBISHI".  Later Mitsubishi PCs had it at a 
                different location.  We hope all early versions had it at this
                location.

                Get Date:       MOV   AH,4
                                INT   1AH
                                Returns CL=year mod 1980, DH=month, and 
                                DL=day all in binary.
                                Also sets AL=0FFH if the clock is busy and the
                                request should be retried.

                Set Date:       MOV   AH,5
                                Load CL, DX as for Get Date.
                                INT   1AH
                                Returns AL=0FFH if busy.

                Get Time:       MOV   AH,2
                                INT   1AH
                                Returns CH=hour, CL=minute, DH=second, and 
                                AL=status.  AL=0FFH means busy.  AL=0 means
                                24-hour mode.  AL=1 means AM and AL=3 means
                                PM.

                Set Time:       MOV   AH,3
                                Load AL, CX, DH as for Get Time.
                                INT   1AH
                                Returns AL=0FFH if busy.

                NOTE:  Some early Mitsubishi PCs came with fixed disk 
                controllers that were not DOS compatible.  In addition to the 
                clock modifications the DOS for those systems also handled the 
                disk controller variants.  If you have such a PC, CLOCK.SYS is 
                not sufficient to enable you to go above DOS level 3.2.  You 
                will also need to replace your fixed disk controller.  I 
                strongly suggest that you create a boot floppy for your current
                DOS level before you try to install your new DOS level.  Then 
                boot your new DOS from a floppy disk, do SYS C: and copy 
                COMMAND.COM to C:, then try a disk boot.  If the disk boot 
                fails, boot the floppy you just created and do a SYS C: and 
                copy COMMAND.COM to C: to restore your old DOS version.  At 
                that point, your best bet is to simply give up and stay with 
                DOS 3.2. If you want to proceed, you must replace your fixed 
                disk controller.

                If SYS C: gives you an error status that indicates that there 
                isn't room for the new DOS version (very possible when moving 
                from 3.2 to 3.3 or above), you must backup your entire fixed 
                disk and use FORMAT C:/S to place the new version of DOS on the 
                disk.  While this is a hassle, at least if your PC won't boot
                from the disk, the fall-back approach is identical.  There will
                be room to put DOS 3.2 or earlier back on the fixed disk.
_______________________________________________________________________________
 6              I/O bus clock.  Used on AST Research boards and others.  
                Typically uses the same I/O base address as type 4.  However
                the clock registers are selected by sending the register
                address to the base I/O address and then reading or writing
                data at the base I/O address + 1.  The internal register
                numbers and their contents are the same as for type 4.

                Automatic determination by probing the address register.  If
                the low-order bit is one, it may be this type of clock or
                type 7.  We then look further to determine if it is type 7.
                If you aren't sure which type of clock you have but believe it
                is type 4, 6 or 7, specify type 8 and automatic probing will
                detect which variant it is.  If at all possible specify the
                base I/O address as that will increase the likelihood that
                the correct determination is made.

                I/O addresses used are (again using 2C0 as the example base
                address):

                    2C0  =  Address register.  Writing a value to this address
                            selects the internal register to read or write.
                    2C1  =  Data register.  Reading or writing this address,
                            reads or writes the internal register previously
                            selected by writing 2C0.

                The internal register numbers are (the values to write to 2C0):

                      1  =  100ths of seconds
                      2  =  seconds
                      3  =  minutes
                      4  =  hours
                      6  =  days
                      7  =  months
                      9  =  month last time date was read or written
                      A  =  year
                      B  =  initialization flag
                     14  =  status
                
                Other processing is the same as type 4.
_______________________________________________________________________________
 7              I/O bus clock.  Used on AST Research boards and others.  
                Typically uses the same base I/O address as types 4 and 6.
                
                Uses a more complex register access sequence than type 6.
                Can be detected by looking to see if the value in register D
                has bit 1 (value=2) set.  If you aren't sure which type of 
                clock you have but believe it is type 4, 6 or 7, specify type 
                8 and automatic probing will detect which variant it is.  If 
                at all possible specify the base I/O address as that will 
                increase the likelihood that the correct determination is made.

                The base I/O address is used as an address register and the
                base + 1 as a data register.  This is the same as for clock 
                type 6.  However, the internal registers and the form of the 
                commands is quite different.  The primary difference is that 
                the internal registers only hold four bits of data each.  Thus 
                each internal register represents a single decimal digit.

                The I/O addresses are used as follows (using 2C0 as an 
                example):

                    2C0  =  Address register.  The number of an internal 
                            register plus 80H is written to this I/O address to
                            select an internal register.

                    2C1  =  Data register.  Four bits of data are read or
                            using this I/O address from or to the internal 
                            register previously selected by writing to 2C0.  
                            
                The internal registers are:

                      0  =  Units digit of seconds
                      1  =  Tens digit of seconds
                      2  =  Units digit of minutes
                      3  =  Tens digit of minutes
                      4  =  Units digit of hours
                      5  =  Tens digit of hours
                      6  =  Day of week
                      7  =  Units digit of day of month
                      8  =  Tens digit of day of month
                      9  =  Units digit of month
                      A  =  Tens digit of month
                      B  =  Units digit of year
                      C  =  Tens digit of year

                      D  =  Function register 
                      E  =  Function register
                      F  =  Function register
_______________________________________________________________________________                
 8              I/O bus clock.  Type unknown.  Probe only for types 4, 6, 7, 
                9, and B.  Use type 8 if you are sure that you have an I/O bus
                (i.e., the clock is on an add-on card) clock but aren't sure 
                whether it is type 4, 6, 7, 9, or B.  If at all possible, 
                supply the base I/O address of the clock as this will greatly 
                increase the likelihood of the correct handling method being 
                chosen.
_______________________________________________________________________________
 9              I/O bus clock.  This type was used by Quadram Corporation on
                the QuadCard, QuadCard II, and QuadCard 512+.  It may have been
                used on others as well.

                Automatic determination checks to see that I/O registers exist
                at 310H or 210H.

                This clock used four I/O control registers and twelve internal
                registers.  The I/O registers (using 310H as the example) are:

                    310  =  Data register (used to move data values)
                    311  =  Address register (used to select internal register)
                    312  =  Function register (Read, write, hold counter)
                    313  =  Control register (Enables read or write function)

                The internal registers are:

                      0  =  Units digit of seconds
                      1  =  Tens digit of seconds
                      2  =  Units digit of minutes
                      3  =  Tens digit of minutes
                      4  =  Units digit of hours
                      5  =  Tens digit of hours - Also uses bit 2 (=4) to 
                            indicate PM if in 12-hour mode and bit 3 (=8) to
                            select 24-hour mode
                      6  =  Day of week (we don't use this)
                      7  =  Units digit of days
                      8  =  Tens digit of days - Also uses bit 3 (=8) to
                            indicate that this is a leap year.  This bit must 
                            be set by software whenever there is less than 366 
                            days until the next leap day.  If you do not boot 
                            within that period, leap day will not be taken.
                      9  =  Units digit of months
                     10  =  Tens digit of months
                     11  =  Units digit of year mod 1980
                     12  =  Tens digit of year mod 1980

                NOTE:  If you have this type of clock, you can only set the 
                time to the nearest minute.  Whenever the time is set, the
                seconds are always set to zero.  You should set the time as
                the minute changes.
_______________________________________________________________________________
 A              AT&T 6300, 6300 PLUS, 6300 WGS

                Automatic probing is accomplished by trying to read the clock.
                If the read attempt using the BIOS is successful (carry flag
                not set), the clock is assumed to be present.

                A base year should be specified on the DEVICE= line.  If it
                is not, 1992 will be used.  This base will be good for all
                dates from 1992-1-1 till 1999-12-31.
                
                Get Date:       MOV   AH,0FEH
                                INT   1AH
                                Returns BX = Days since base,
                                CH = Hours, CL = Minutes, DH = Seconds,
                                DL = 100ths of seconds

                Set Date:       MOV   AH,0FFH
                                MOV   BX,Days since base
                                MOV   CH,Hours
                                MOV   CL,Minutes
                                MOV   DH,Seconds
                                MOV   DL,0
                                INT   1AH
_______________________________________________________________________________
 B              Hyundai 8088 clock.  

                Automatic determination probes the control registers.  If they,
                appear to be present, CLOCK tries to read the clock.  Legal 
                time and date values will select this clock.

                This clock uses I/O addresses E0H through EFH as follows:
                        E0      Units digit of seconds
                        E1      Tens digit of seconds
                        E2      Units digit of minutes
                        E3      Tens digit of minutes
                        E4      Units digit of hours
                        E5      Tens digit of hours
                        E6      Day of week
                        E7      Units digit of days
                        E8      Tens digit of days
                        E9      Units digit of month
                        EA      Tens digit of month
                        EB      Units digit of year
                        EC      Tens digit of year
                        ED      Control
                        EE      Control
                        EF      Control
_______________________________________________________________________________

REVISION HISTORY:

920411 -        Version 2.22: Changed order of probing to probe memory-
                mapped clocks last as they are being spuriously found on 
                some Tandy systems.

920401 -        Version 2.21:  Changed pattern of I/O address probing to 
                probe all possible I/O addresses for one type (e.g., 4)
                before trying any for another type.  Try to avoid finding
                the wrong type.  Added the type B clock to the type 8 probe.

920328 -        Version 2.20:  Changed order of I/O address probing for clock 
                types 4, 6, and 7 to avoid, where possible, accessing other
                boards.  Most commonly used I/O clock addresses, I hope, are
                now probed first.

920322 -        Version 2.19:  Improved probing for I/O clocks to check that
                legal values are found in all the data registers.  Several of
                the I/O clocks use operation sequences so much like each other
                that it is possible to choose the wrong one if we don't 
                actually read the time and date and see if the values are 
                legal.  This approach to probing may possibly result in not 
                finding a clock that is present but that has been totally 
                reset.  Such a clock should be found on a second try to boot 
                with CLOCK.SYS as the counters will have advanced by then.

920320 -        Version 2.18:  Added probing for generic PC/AT type clock on
                systems that don't have the PC/AT signature in the BIOS.

920307 -        Version 2.17:  Added Hyundai 8088 clock.

920112 -        Version 2.16:  Added AT&T 6300 clock.

920111 -        Version 2.15:  Fixed memory address used by one type of SMT 
                No-Slot clock.

920105 -        Version 2.14:  Added support for a wider variety of memory
                mapped clocks including the SMT (Systems Manufacturing
                Technology) No-Slot clocks.

911208 -        Version 2.13:  Add probing for Vendex Headstart Turbo-888-XT
                system and any other I/O clock at 300H.  Change I/O clock 
                probing logic to make it less likely to find the wrong type
                by accident.

911129 -        Version 2.12:  Fix handling of Quadram clocks (type 9).
                They can only set seconds to zero so generate an error
                if anyone tries to set the seconds to any other value.

911128 -        Version 2.11:  Fix bug in handling clock type 9, Quadram
                clocks that left clock turned off after operations.  Also
                fix bug in busy determination for clock types 4 and 6 that
                could result in a decision that the clock was not operational.

911121 -        Version 2.10:  Add clock types 6 ,7 and 9.  Add type 8 to do
                specific probing for the various I/O bus clock types.

911109 -        Version 2.05:  Fix bug in leap day handling for I/O clocks.
                Fix bug that caused hung systems when setting the date or 
                time on Z-18x portables.

911026 -        Version 2.04:  Add support for I/O clocks at addresses 240H
                and 340H.  Reduce resident memory required by clock driver to
                only that required for specific clock type.

911021 -        Version 2.03:  Change handling of new day flag from BIOS to
                accommodate BIOSs that indicate multiple days have passed.

911020 -        Version 2.02:  Fix bug in returning date on clock read
                functions.  Added message in automatic determination to
                indicate type found.

911010  -       Version 2.01:  Added automatic determination of Mitsubishi
                8088 PC clocks.  Fixed handler to keep the BIOS counter set
                properly for programs that read it directly.  Also returns a
                finer granularity value (100ths of seconds) on reads.

911009  -       Version 2.00:  Modified clock driver to support additional
                clock types.  Thanks to Eric Smith (no relation) for help in 
                finding out how the Zenith PC clock worked.

911005  -       Version 1.20:  Changed prologue and epilogue to conform to
                DOS 5.00 documentation.  Seems to work OK with DOS 5.0 
                without the changes, but we might as well be consistent to
                save problems later.

910903  -       Version 1.10:  Added display of current date and time when
                initializing.

910518  -       CLOCK version 1.00.  Initial version developed at the request
                of a friend with a Sperry PC/HT who wanted to move to DOS 4.01.

1984    -       Write clock device driver for AST clock for IBM PC-1.  This
                serves as the introduction to what device drivers and 
                especially the CLOCK$ driver are all about.