The Truth About Hard Drives
                (How to Purchase Hard Drives intelligently)


Author:

Joseph J. Tamburino
7 Christopher Road
Westford, MA 01886
(508) 692-7756
CompuServe:  70033,107
A member of Channel 1 BBS, Cambridge, MA (call 411 or 1-555-1212)


I was formatting some hard drives the other day, doing some arithmetic
on the format specifications, when it finally struck me.  Maybe I'm a
slow learner or something, but it took me a good number of years before
I realized the truth;  Hard drive manufactures LIE about the amount of
storage space a given hard drive has.  I always knew that the BIOS
calculations for drive storage didn't quite match the manufacturer's
published size, but I never bothered to figure out exactly why ...
until today.  But before tell you the scoop, let me give you a brief
overview of hard drive geometry.  A picture would help here, but
I don't feel like drawing one at this moment, so you're going to have
to use your imagination.  Anyhow, instead of having information handed
to us all the time, sometimes its good idea to construct it ourselves,
if only to preserve our mind's ability to create and learn ...

(Ok, so that's a sorry excuse not to include a picture).

If you open up a hard drive (not a good idea, unless it's already
broken), you will find at least one large round plate.  I'm not sure
what the real term they use is, but I guess "platter" or "disk" are
both appropriate terms for these things.  Probably you will see at
least two of these plates, although you may see three, four, or even
more stacked on top of each other (piggybacked).

Actually, the idea of stacking multiple magnetic disks on top of each
other is not at all new, but dates back many years ago when the disks
were housed in these huge machines that looked like washing machines
(literally), and probably had 600 MEGs of storage (tops).

But now, these platters are all squished into these little boxes that
we call hard disks.  Anyhow, each of these platters has at least one
head (attached to an arm, not unlike the arm of a floppy drive, and
remotely like the arm of an LP player).  You may be surprised to learn
that even though all platters have two recording surfaces (or CAN have
two recording surfaces), not all surfaces have to be utilized in a
given hard drive.  In fact, this is ALWAYS the case in a hard drive
with an odd number of heads.  I mean, if your hard drive has 5 heads,
then it must be quite obvious that at least one side of one platter is
not being utilized at all!  [What a ripoff!].  This is done to conserve
space.  I mean, if you can't fit an extra head between the case of the
drive and the last platter surface, without oversizing the drive, then
you're outta luck.

Ok, but we're not done yet.  Obviously (I hope), you know that the
heads of the disk drive are free to move up and down the surface of a
platter.  That movement, combined with the rotation of the set of
platters, enables each head to "visit" almost the entire surface of
that head's platter.  (Read this sentence over again, if you don't
understand.  If you have to, draw a picture.  You'll get the hang of
it).

Here's where a picture would help alot.  Your drive heads move up and
down the platter surfaces at fixed intervals while the drive spins at a
constant rate.  At each interval, each head is able to read a full
"circle" of information.  Take a piece of paper and move the paper in
such a way that a pen (at a fixed location), causes a rough sketch of a
circle to be drawn on the paper.  In this fashion, the pen is like the
head of a hard drive.  Now lift the head (pen) and move it to a new
location on the paper.  Now rotate the paper again to produce another
circle.  (The center of rotation MUST remain the same).  You have just
drawn two of what are known as "tracks" or "cylinders" in drive
terminology.


Cylinders Explained
-------------------

So why in heck are those paths called cylinders when they are circular.
Well technically, they are not.  Really, when you are describing a
path made by one head at a fixed location, you are talking about a
"track".  The term "cylinder" is really used to describe the path made
by a SET OF HEADS on a SET OF PLATTERS.  In other words, if you took an
array of disks (let's say LP's), and then used a really sharp knife to
cut a circular path in those disks around the center point, the middle
portion would be in the shape of a cylinder.  (Actually, you don't need
to cut the disks at all to get a cylinder; but by cutting them you can
achieve smaller and cylinders.  This should demonstrate exactly what is
meant when a hard drive manufacturer talks of cylinders -- smaller and
smaller rings cut out of a stack of disks, forming cylinders).

This also explains why in floppy disk drive terminology, they talk
about "tracks" instead of cylinders; disk drives only have one platter,
so the only shape you can visualize is a circle [or a mighty flat
cylinder, which is why the term "cylinder" can still be used when
describing floppy disk drives and single-platter hard drives].



Sectors Explained
-----------------

Sectors are easy.  Unlike platters, heads, and cylinders which are
defined by the physical makeup of the disk, sectors are described
arbitrarily.  You see, platters can be visibly located and counted as
soon as you open up a hard drive, and heads can be counted upon
further examination.  Cylinders can also be counted by counting the
number of individual steps that the set of heads makes across the
platters.

But sectors are different.  Sectors are defined in software, or at
least by the program imbedded in your hard drive's controller card, or
other such place.  A sector is almost ALWAYS defined in the world of
hard drives as being a collection of 512 bytes.  The size of a sector
rarely, if at all, changes.  But what does change is the density of
sectors.  I.e, the number of sectors you can cram onto one track
of a platter.

In the MFM world, drives normally cram around 17 sectors per track onto
the platter.  In the IDE world, this number varies, but can be around
30 to 35, or more.  Obviously, the more 512-byte sectors that a
manufacturer can cram onto a given track, the more storage the drive
will be able to deal with.

Now I mentioned earlier that sectors are defined arbitrarily by 
software.  That is true, but the number isn't as arbitrary as it may 
seem.  A hard drive manufacturer has to run the drive through thousands 
of tests before deciding on a good number of sectors for a certain 
drive.  If the manufacturer tries to cram too many sectors on a track, 
the drive may become unreliable.  In some cases, however, it is 
possible for a knowledgeable programmer to change the sector density on 
his / her drive.  Most likely, with poor results, I would guess.

--------------------------------------------------------------------------
The lie explained.  Finally!
----------------------------

Now that the geometry lecture is over, the rest is easy.  The
calculation you perform to get size of your disk drive is simple:

size = cylinders x heads x sectors/track x 512

Notice that I say "sectors/track" and not "sectors/cylinder".
Sectors/track is what the drive manufacturer will report in their
specs, and is what you should use.  Sectors/cylinder is useless.
Note that the "512" represents the bytes/sector which typically is 512,
in most operating systems and drive technologies.

So let's say your Spiffy brand hard drives has these specs:

Cylinders:       1024
Heads:           5
Sectors / Track: 17

Then, 1024 x 5 x 17 x 512 = 44,564,480 bytes.  Now how would you report
that number if you were the drive manufacturer?  Well, first you would
scale the number down by dividing by 10 ^ 6 (10 to the power of 6, or
1000 * 1000), which would leave you with 44.56448 MEG.  Then you would
round upwards and report the drive as a 45 MEG drive.  This is exactly
how one of my MFM drives was reported.

THE LIE:  But in computer terminology, a megabyte is NOT 10 to the
sixth power!  A megabyte is not 1,000,000.  It is not.  Not.  Not.
Period.  A megabyte is 1024 * 1024, or 1,048,576.  This is one MEG of
bytes.  This is what DOS thinks one MEG is.  This is what ALL computers
think one MEG is.  The difference between 1,000,000 and 1,048,576 is
48576 bytes, or 47.4K!!!!  Early PCs didn't even have 47.4K!

The number of megabytes that this drive really has is:

          44,565,480 / 1,048,576 = 42.5 (and some change)

This is really how many MEGS of storage you have.  The difference
between the reported size and the actual size is 2.5 MEG.  2.5 MEG is
still alot of storage, even in today's world.  A lot of good Window's
apps can reside safely in 2.5 MEG or less.  In short, you are paying
for 2.5 MEG that doesn't PHYSICALLY exist on the system.


Another example
---------------

I have an IDE drive that the manufacturer claims supported 105 MEG.  I
went absolutely nuts trying to find that 105 MEG, 5 of which I finally
figured out to be absolutely nonexistent!

The Specs are:

Cylinders:      979
Heads:          6
Sectors/Track:  35


Do the math:

          979 x 6 x 35 x 512 = 105,262,080

                Looks like 105M, right?  Wrong!

          105,262,080 / 1,048,576 = 100.4 MEG (rounded).

So 105 - 100.4 = 4.6 MEG which are absolutely nonexistent.  It took me 
forever to figure out where the missing five megs were!!!  After all, 
we are talking about 4.83% of the storage space here!


                     When shopping, DO THE MATH!

-------------------------------------------------------------------------

One last note:


Don't get confused when people talk about "unformatted" and "formatted" 
capacity.  This is NOT the issue I just discussed here.  What I just 
discussed here was lies, plain and simple.

Unformatted capacity represents "total" storage, without regards to how 
the operating system formats the disk.  Unformatted capacities are 
generally only discussed in regards to floppy disks, where there is no 
precisely set standard on how the disks should be formatted.  

Hard drives, on the other hand, are precisely defined, and are 
generally only formatted according to the manufacturer's 
specifications.  In other words, if a drive has 1024 cyls, 5 heads, and 
17 sects / track, that is the number you'll use, as that is the number 
the manufacturer came up with.  Again, the "sectors/track" is the only 
variable here.  But generally, if the manufacturer says 17 secs/track, 
you'll use 17 secs/track.


Again, the only time you'll worry about "unformatted" vs. "formatted" 
capacities is with floppy disks, where the electronics are defined in 
the drive, but not the media itself.  I.e., low density 3.5" diskettes 
are around 800K unformatted capacity, but DOS tends to think of them as 
being 720K, because DOS is weird.


I'd like to hear your opinions!

-- Joe