SETCLOCK V0.2
                                        Preliminary Documentation Apr 19/90

SETCLOCK is a utility which uses the Heathkit GC-1000 "Most Accurate Clock"
to set you  PC's date and time according to  a world standard cesium-atomic
clock.  The GC-1000 must be equipped  with the optional Heathkit GCA-1000-1
computer interface.

SETCLOCK allows several  features and options in addition  to those offered
by the GC-1000:

    - Sets  your PC's  date and  time very  accurately with  or without  an
      audible signal for confirmation.

    - More flexible time-zone and propagation delay settings.

    - Automatic or manual setting of PC's date and time.

    -  Display of  time  error incurred  by PC's  clock  compared to  world
      standard time.

    - Continuous  display of local,  UTC (Universal Coordinated  Time), and
      PC time to 1/10 second accuracy.

    - Automatic and/or manual adjustment of year without having to take the
      GC-1000 appart to change hardware switches.

    - Display of  time in 12-hour or 24-hour format  independent of GC-1000
      display mode.

---------------------------------------------------------------------------

Operation
---------

SETCLOCK.EXE is a stand-alone program which can be invoked using any one of
three methods:

1)
    From the DOS  prompt by typing "SETCLOCK".  This allows  the setting of
    various parameters on a configuation screen.

2)
    By a  batch file.  By checking  "errorlevel", a batch  command sequence
    can determine  whether the PC's date  and time have been  properly set.
    Eight distinct conditions are available.

3)
    From within another program.  Executing SETCLOCK  from a "C", BASIC, or
    other program, the date and time can always be set correctly.


                             S.K. Consultants
                                                                          1






                                                              SETCLOCK V0.2
                                        Preliminary Documentation Apr 19/90

SETCLOCK will maintain a small configuration  file SETCLOCK.CFG to hold the
user selected options.  

To get started just type "SETCLOCK" at the DOS prompt.

In  the  absense   of  a  configuration  file,  SETCLOCK   will  present  a
configuration  screen.  Sixteen  (16)  seperate parameters  may  be set  to
customize the operation of program.  These parameters are described below.



Item                        Possible values
----                        ---------------

Serial port                 COM1, COM2
Baud rate                   110, 150, 300, 600, 1200, 2400, 4800, 9600
Current year                1990 to 2037
UTC override preset         YES or NO
Time zone preset            -11:00 to +12:00 (1 hour incr.)
Propagation preset          0 to 3750 (250 mile incr.)
DST adherence preset        YES or NO
Tome zone actual            -15:45 to +15:45 (15 minute incr.) or "same"
Propagation actual          0 to 8188 miles (2 mile incr.) or "same"
DST adherence actual        YES or NO
PC set HI-SPEC only         YES or NO
PC set DATE & TIME          YES or NO
PC set signal               YES or NO
Auto read                   YES or NO
Hours display mode          12 or 24
Configuration screen        YES or NO


Select the  item you wish  to change by pressing  the "up" or  "down" arrow
keys. Once the item is selected, press  the "left" or "right" arrow keys to
change its value to one of the possible values listed above.

Esc - Pressing the ESCAPE key will exit the program.

F1  - Function key 1 will cause the GC-1000 to send data to the PC.

F2  - Function key 2 will set the PC's date and time.



Each of the configuration items are described in detail next.




                             S.K. Consultants
                                                                          2






                                                              SETCLOCK V0.2
                                        Preliminary Documentation Apr 19/90

Serial port:        

                    Choose the appropriate serial port to which the GC-1000
                    will be connected.   Normally this will be  COM1.  Some
                    PCs  are equipped  with ports  COM3 and  COM4 as  well.
                    These  ports are  not  standardized  and are  thus  not
                    supported in this software version.

Baud rate:

                    Select  the  baud rate  to  match  the rate  chosen  by
                    switches in  the GC-1000.  It  is usually  desirable to
                    use  the highest  baud  rate  available.  The  selected
                    rates must match  in order for the sofware  to read the
                    GC-1000.  The  accuracy of time  in unaffected  by this
                    data rate.

Current year:

                    The GC-1000 provides  switches for setting the  year in
                    the range 1983  to 1998.  Unfortunately the  clock must
                    be opened every year in order to update these settings.
                    And what about after 1998?  By setting the current year
                    parameter this software will  provide the correct date.
                    The year  is also updated automatically.   The internal
                    setting of the GC-1000 is effectively ignored.

UTC override preset:

                    A switch on the GC-1000  allows it to display Universal
                    Coordinated Time.  If this is  set, it also affects the
                    data  transmitted to  the PC.   Set  this parameter  to
                    match the  switch setting (YES  or NO) so  that correct
                    local time and UTC is calculated.

Time zone preset:

                    Five switches on the GC-1000  select one of twenty-four
                    time zones  relative to  UTC: -11:00  to +12:00  hours.
                    Set this  parameter to  match the  setting of  the time
                    zone as represented by the switches.

Propagation preset:

                    The propagation  delay is set  by four switches  on the
                    GC-1000.  Set  this parameter to  match the  setting of
                    the switches.


                             S.K. Consultants
                                                                          3






                                                              SETCLOCK V0.2
                                        Preliminary Documentation Apr 19/90

DST adherence preset:

                    The  GC-1000 can  be set  to  adjust automatically  for
                    Daylight Saving  Time.  Select this parameter  to match
                    the present setting of the switch (YES or NO).

Time zone actual:

                    Select this parameter  for the time zone  in your area.
                    This setting provides a more accurate and wider ranging
                    set of values that of the  GC-1000.  Believe it or not,
                    some  localities differ  from UTC  by  14 hours!   Some
                    places are  not on  the hour  - like  Newfoundland (1/2
                    hour).  Other regions are out by 1/4 hour.

Propagation actual:

                    This  parameter  allows  a  more  accurate  setting  of
                    distance to Ft.  Colins, Colorado.  Set this  option if
                    you know the exact distance and wish even more accurate
                    time.

DST adherence actual:

                    Set this  parameter according to whether  your locality
                    conforms to Daylight Saving Time.  During summer months
                    when  this  is in  effect,  you  can also  change  this
                    parameter to  see what  time it  was before  the clocks
                    were changed.

PC set HI-SPEC only:

                    Set this  parameter to YES if  you wish your  PC's date
                    and time to be updated only when the GC-1000 has locked
                    into the  world standard and  is accurate to  within 10
                    milliseconds.  Selecting  NO causes ths software  to be
                    less descriminating,  and sets  PC whether  or not  the
                    GC-1000 has been synchronized lately.

PC set DATE & TIME:

                    Set this parameter to YES if you want your PC's time to
                    be updated  once data is  read from the  GC-1000.  This
                    setting is only  in effect during "Auto  read" or while
                    the configuration screen is OFF.




                             S.K. Consultants
                                                                          4






                                                              SETCLOCK V0.2
                                        Preliminary Documentation Apr 19/90

PC set signal:

                    Set this parameter  to YES if you wish  an audible tone
                    to confirm setting of the PC's  date and time when that
                    occurs.

Auto read:

                    Set this parameter  to YES if you want  the software to
                    periodically read the GC-1000 date  and time and update
                    the screen  accordingly.  The  PC's date  and time  are
                    also periodically  synchronized if the  "PC set  DATE &
                    TIME" parameter is YES.

Hours display mode:

                    Set this parameter  to 12 hour mode  (North American AM
                    or PM is displayed instead of 1/10's of seconds), or 24
                    hour mode wich is internationally recognized.

Configuration screen:

                    Set this parameter to YES if you want the configuration
                    screen the next time SETCLOCK  is run.  Setting this to
                    NO is  useful if SETCLOCK is  run from a batch  file or
                    executed  from  another  program.   No  information  is
                    displayed on  the screen, but the  PC date and  time is
                    updated  according to  other  parameter settings.   The
                    program  returns  a  status code  allowing  batch  file
                    commands or other programs to know what happened.

Status codes:
        0   - Program was executed in "interactive" mode where the
              configuratuion screen was shown.
        1   - Communications error prevented the program to successfully
              read the GC-1000.  Check all cables, baud rate settings, etc.
        2   - GC-1000 synchronized & HI-SPEC indication.

        3   - GC-1000 synchronized but not HI-SPEC.  The clock is not
              guaranteed to be accurate.
        4   - GC-1000 is not synchronized to time signal.  It has just been
              plugged in and as yet does not know the correct time.
        5   - Failure to read SETCLOCK.CFG file.

        6   - Like condition 2, and PC date & time have been updated.

        7   - Like condition 3, and PC date & time have been updated.


                             S.K. Consultants
                                                                          5