SOKKISHA.EXE  (Version 6.01, April, 1992)
************

Field of Application:
     Land Surveyors who use the Sokkisha Total Station and its
     SDR2 Electronic Field Book.

Purpose:
     Transfer data from the Electronic Field Book to the computer.

Operation:
     The program will create two files of the same data:
          JOBid.RAW:  unmodified data as received from the EFB.
          JOBid    :  translated data in a concise format.

     If you have two Serial Ports, you must connect to #2.

     Baud Rate of the EFB must be set at 4800. (Parameters)

Related Programs:
     SOKKSET : program to transfer Coordinates into the SDR2 for
               use in the Setting-Out program.

     SOKKPLOT: utility program to load the SDR2 plotting routine.

Registration:
     This is a Shareware program.  If you find it useful, you should
     register your copy by sending $20 to:

               Lorne Davidoff, P.Eng.
               R3, Stouffville, Ontario
               Canada, L4A 7X4

     Your support of the Shareware concept will make quality
     software available at reasonable prices!