CREATIVE PORTFIX 82C710
                                    version 1.00

                                 Creative Labs, Inc.
                                    15 June 1992

    Description:
    ------------
       PORTFIX was written to enable the serial and parallel ports on
       motherboards with the Chip & Technologies 82C710 Universal Peripheral
       Controller and an installed Sound Blaster board.

       This program turns on the serial port (3F8h) and the parallel port
       (378h) if it is not already provided on an external card.  If they
       are already on an external board then the on-board ports will remain
       unavailable.


    Installation:
    -------------

       Using your favorite editor, place PORTFIX in the AUTOEXEC.BAT file 
       before any programs which use the serial port.  This includes mouse 
       drivers, fossil drivers, and communication programs.

            BEFORE                               AFTER
            ------------------------             ------------------------
            echo off                             echo off
            cls                                  cls
            prompt $p$g                          prompt $p$g
            path=c:\;c:\dos;c:\utils             path=c:\;c:\dos;c:\utils
            mouse.com                        --> PF82C710.COM
                .                                mouse.com
                .                                    .
                .                                    .
                                                     .

        This is an example of the 82C710 initializing properly:

            Creative Port Fix I (82C710), version 1.00
            Copyright (c) Creative Labs, Inc., 1992.  All right's reserved.
                    Configuration Port moved to 3A0.
                    COM1 was turned on.

        Only COM1 was initialized here but LPT1 or LPT2 (monochrome only)
        may be also be initialized.


    Errors:
    -------

       Invalid command line:

          1. A non-hexidecimal value or zero was entered.
                Fix: Use default (no command line) or hexidecimal address.

          2. More than one option was given on the command line.
                Fix: Use default (no command line) or only one option.


       Error - 82C710 chip not detected in your system:

          1. 82C710 chip is not used.
                Fix: Use different version of PORTFIX.

          2. The port address (default: 3A0h) conflicts with another device
             in the system.
                Fix: Use different address.


       Error - Serial port (COM1) did not initialize:

          1. 82C710 chip on the motherboard is bad.
                Fix: Repair motherboard or purchase an I/O card.


       Error - Parallel port (LPT1) did not initialize:

          1. 82C710 chip on the motherboard is bad.
                Fix: Repair motherboard or purchase an I/O card.

     *********************************************************************
     *                                                                   *
     * NOTE: If there are no errors reported but the port still will not *
     *       turn on then there must be another card using that port's   *
     *       address.                                                    *
     *                                                                   *
     *********************************************************************


    Command Line Options:
    ---------------------

       Only one command line option is available.  If neccessary, the port 
       address may be changed by listing the port address you wish to use 
       after the filename.

       Examples:   PORTFIX1 3A0 (default)
                   PORTFIX1 210
                   PORTFIX1 230
                   PORTFIX1 360
                   PORTFIX1 370