QLIB's SYSTEM routines detect the presence or status of PC hardware
     or software.  Monitor type, co-processor presence, CPU speed and keyboard
     toggles may be determined, CPU speed toggle and keyboard toggles may be
     set.  CTRL, ALT and SHIFT key status may also be monitored, and the
     software enviornment may be determined.



 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

     Subroutines: CapsOFF, CapsON
     object file: kbd2.obj

          Simplified controls to toggle the CapsLock key.  See also
     GetKBDToggle and SetKBDToggle.

     Example:
          CALL CapsON         ' this turns Caps Lock on



 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

    Function: oops% = DOSError
    object file: q$error.obj

    DOSError returns an error flag resulting from the most recent QLIB
    subroutine which updates the DOS error flag (see FLoad in DISK.DOC).
    NOTE: not all QLIB subroutines update DOSError!!

    common MS-DOS error codes are:

    2 = file not found
    3 = path not found
    4 = too many open files
    5 = access denied (file may be read-only or a subdirectory
                       or subdirectory not empty)
    8 = insufficient memory
    19= disk is write-protected

    Example:
     REM $INCLUDE: '\qb4\qlib.bi'
     filename$ = "\ramfont\italics.fnt"
     iseg% = fload (filename$)
     IF DOSError THEN
         .
         .
         .              ; error handling code


 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

    Subroutine: EGAinfo(crt%, memory%)
    object file: egainfo.obj

         EGAinfo determines the type of monitor and amount of memory
    installed on an EGA card.  Crt% = 0 if a monochrome monitor is
    attached to the EGA card, -1 if an RGB color monitor, and crt% = 1
    if the monitor is an Enhanced or Mutli-scan monitor.  Memory% returns
    the kbytes installed on the card.  If no EGA is installed, memory% = 0.

    Example:
         CALL EGAinfo(crt%, memory%)



 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

    Function: a$ = EXEName$()
    object files: exename.obj (strncpy.obj)

    requires DOS version 3.0 or later

         EXEName$ returns the full drive and path name of the currently
    executing program.  When developing programs within the QB or QBX
    development enviornment, EXEName$ returns something like:

    C:\QB4\QB.EXE

    Example:
    REM $INCLUDE: 'qb4\lib\qlib.bi'
    PRINT EXEName$                   ' prints name of program


 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

    Subroutine: FindMONO(crt%)
    object files: findmono.obj (find6845.obj, egainfo.obj, q$herc.obj)

         FindMONO determines if a monochrome monitor is installed.
    GetCRT (below) determines the default monitor; FindMONO will
    find an MDA or HGC monitor in single- or dual-monitor setups
    whether the monochrome monitor is default or not.  Crt% = 0 if
    MDA, 128 or greater if HGC or compatible, and -1 if no monochrome
    installed.

    Example:
         CALL FindMONO(crt%)




 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

    Function: Floppies
    object file: floppies.obj

         FLOPPIES determines the number of floppy drives installed in the
    computer.

    Example:
         REM $INCLUDE: 'qlib.bi'
         fdrives = floppies            ' get number of floppy drives


 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

    Function: FloppyType(d%)
    object file: floptype.obj

         Determines the type of floppy disk drive installed.  Drive number
    d% is the BIOS drive number corresponding to the physical drives
    installed:  for drive A, d% = 0, and for drive B, d% = 1.

    Returns:   0 if drive not installed
               1 if drive is 360 k
               2 if drive is 1.2 M
               3 if drive is 720 k
               4 if drive is 1.44M
    Example:
         REM $INCLUDE: 'qlib.bi'
         ' drive a:
         d% = 0
         drivetype = FloppyType(d%)




 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

    Function: GetCMD$(a%)
    object files: getcmd.obj (strndup.obj)

         GetCMD$ isolates and returns command-line parameters without
    converting the parameter to upper case.  GetCMD$ acts like an array
    of strings; GetCMD$(0) returns the first parameter, while GetCMD$(n%)
    returns the (n+1)th parameter.  GetCMD$ returns a NUL string if there
    are no more parameters.

    Note: in the QuickBASIC development enviornment, GetCMD returns QB's
    parameters (including /L and QLIB), while when your program is run
    from the command line, GetCMD$ returns your program's parameters.

    Example:
        REM $INCLUDE: 'qlib.bi'
        ' print command line parameters, starting with the first one
        a% = 0

10:     c$ = GetCMD$(a%)
        IF c$ <> "" THEN PRINT c$: GO TO 10



 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

    Subroutine: GetCPU(cpu%)
    object file: getcpu.obj

         Determines the processor in the computer system.  Returns cpu% = 0
    if 8086 or 8088, cpu% = 1 if 80186 or 80188, cpu% = 2 if 286, cpu% = 3
    if 386 or 386sx, and cpu% = 4 if 486.

    Example:
         DIM cpu$(4)
         FOR i = 0 to 4: READ cpu$(i): NEXT i
         DATA "8086 or 8088","80186 or 80188","286","386","486"
         CALL GetCPU(cpu%)
         PRINT cpu$(cpu%)



 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

    Subroutine: GetCRT(crt%)
    object files: getcrt.obj (q$herc.obj, egainfo.obj)

         GetCRT tells you what kind of display is being used.  The returned
    value will be zero if it's MDA or EGA with a monochrome monitor, -1 if
    CGA, 1 if EGA with a color or enhanced color monitor, 2 if MCGA, and if
    VGA, crt% will be 3.  With Hercules or Hercules clones, crt% will be 128
    or greater.  The Hercules Graphics Card Plus returns 144, and the 
    Hercules InColor card returns 208.  See also IsSEVGA, EGAinfo, and
    FindMONO.

    Example:
         REM $INCLUDE: 'qlib.bi'
         CALL GetCRT(crt%)
         SELECT CASE crt%
              CASE -1
                   PRINT "CGA Color"
              CASE 0
                   PRINT "Monochrome Display Adapter"
              CASE 1
                   PRINT "EGA"
              CASE 2
                   PRINT "MCGA"
              CASE 3
                   PRINT "VGA"
              CASE 128 TO 208
                   PRINT "Hercules"
         END SELECT



 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

    Subroutine: GetDOSVer(maj%, min%)
    object file: dosver.obj

         GetDOSVer returns the major and minor version numbers of the DOS
    installed.  Maj% is the major version number, i.e., maj% = 3 if DOS 3.xx
    is installed.  Min% is the minor version number, i.e., min% = 21 if DOS
    x.21 is installed.

    Example:
     CALL GetDOSVer(maj%,min%)
     REM if maj% < 3 then SHELL may not be reliable


 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

    Subroutine: GetKBDToggle(kbd%)
    object file: kbd.obj

         Returns the status of the keyboard toggles and whether the CTRL, ALT
    or SHIFT keys are pressed.  The code returned by GetKBDToggle is a copy of
    the BIOS keyboard status byte, which must be ANDed to determine which key
    toggles are set.  See also SetKBDToggle.

    Example:
         rshift% = 1
         lshift% = 2
         shiftkey% = 3
         ctrl% = 4
         alt% = 8
         scroll% = 16
         numb% = 32
         caps% = 64
         insert% = 128
         
         CALL GetKBDToggle(kbd%)
         IF (kbd% AND rshift%) THEN PRINT "Right Shift pressed"
         IF (kbd% AND lshift%) THEN PRINT "Left Shift pressed"
         IF (kbd% AND shiftkey%) THEN PRINT "Shift Key pressed"
         IF (kbd% AND ctrl%) THEN PRINT "Ctrl Key pressed"
         IF (kbd% AND alt%) THEN PRINT "Alt Key pressed"
         IF (kbd% AND scroll%) THEN PRINT "ScrollLOCK ON"
         IF (kbd% AND numb%) THEN PRINT "NumLOCK ON"
         IF (kbd% AND caps%) THEN PRINT "CapsLOCK ON"
         IF (kbd% AND insert%) THEN PRINT "INSERT ON"




 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

    Subroutine: GetSpeed(speed%)
    object file: speed.obj

         Determines whether the system is in "turbo" mode.  Returns 0 if
    CPU is operating at normal speed, 1 if operating at faster CPU speed.
    See also SetSpeed.

    Example:
         CALL GetSpeed(speed%)


 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

     Function: IsATT
     object files: isatt.obj ($6845.obj, egainfo.obj)

     IsATT determines if the program is running on an ATT 6300 or similar
     computer (such as Olivetti).  If a Hercules is also installed in
     the computer it may be switched to HALF mode (see Use32k, Use64k in
     GRAPHICS.DOC).

     Example:
          REM $INCLUDE: 'qlib.bi'
          REM  look for ATT 6300 so I can use graph mode &H40
          REM  which is twice the resolution of CGA 2-color mode

          modenumber% = 6                   ' assume CGA
          IF IsATT THEN modenumber% = &H40
          CALL ScreenMode(modenumber%)      ' see GRAPHICS.DOC


 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

     Function: IsMSHERC
     object file: ismsherc.obj

     IsMSHERC determines if the MSHERC.COM resident Hercules driver
     has been installed.  (MSHERC.COM is called QBHERC.COM in early
     versions of QB 4.x).  MSHERC.COM is required to use BASIC's
     SCREEN 3 function.  MSHERC is not required for QLIB's Hercules
     graphics subroutines.

     IsMSHERC returns 0 if MSHERC has not been loaded, or returns -1
     if MSHERC has been loaded.

     Example:
         REM $INCLUDE: 'qlib.bi'
         IF IsMSHERC THEN ...     ' use either QLIB or BASIC Hercules stuff

            


 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

     Function: IsSEVGA
     object file: issevga.obj

          IsSEVGA determines if a Super EGA or Super VGA graphics
     card is installed.  Systems detected are:

     Everex Micro Enhancer EGA
     Paradise EGA 480
     Oak VGA
     Paradise Plus 16 VGA
     Tseng VGA
     Western Digital VGA

     Note that IsSEVGA does not determine what kind of monitor is
     connected to the card.  Many Super EGA/VGA cards require a
     multi-frequency monitor to take advantage of the card's extended
     capabilities.

     IsSEVGA returns 0 if no supported system is detected.  If a
     Super EGA/VGA is detected, IsSEVGA returns:

     Super EGA:    256+1 if Paradise EGA 480
                   256+2 if Everex Micro Enhancer

     Super VGA:    768+1 if Paradise Plus 16
                   768+3 if Tseng VGA
                   768+4 if Oak VGA
                   768+5 if Western Digital VGA

     Example:
          REM $INCLUDE: 'qlib.bi'
          evga% = IsSEVGA
          if evga% THEN ...  'ask user if he/she has a multi-frequency
                             ' monitor attached to the computer



 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

     Subroutines: InsertOFF, InsertON
     object file: kbd2.obj

          Simplified controls to toggle the Insert key.  See also
     GetKBDToggle and SetKBDToggle.

     Example:
          CALL InsertON       ' this turns Insert key on



 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

    Function: KBDType
    object file: kbd1.obj

        Detects enhanced (101-key) keyboards.  Returns 1 if 101-key
    keyboard present and supported, 0 if not.  NOTE: KBDType returns 1
    only if the enhanced keyboard is present AND is supported by the
    computer's BIOS.

    Example:
         REM $INCLUDE: 'qlib.bi'
         IF KBDType THEN PRINT "Enhanced keyboard attached to system"



 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

     Subroutine: KeyRate(delay%, repeat%)
     object file: keyrate.obj

          KeyRate changes the keyboard's "typematic" delay and repeat rate
     on PS/2 and most AT computers.  Delay% (0 - 3) sets the delay time for
     the start of the typematic action.  Repeat% (0 - 31) sets the number
     of repeats per second.  For both delay% and repeat%, 0 gives the fastest
     keyboard action, and the maximum value (delay% = 3, repeat% = 31) gives
     you an unbearably slow keyboard.

     Example:
          REM  don't slow me down!!
          delay% = 0: repeat% = 0
          CALL KeyRate(delay%, repeat%)





 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

    Function: a% = MathChip
    object file: mathchip.obj

         Detects the presence of a math coprocessor in the system.
    Value returned = 0 if not installed, 1 if 8087, 2 if 80287, 3 if 80387.
    DECLARE FUNCTION MathChip%() before using MathChip.  The INCLUDE
    file QLIB.BI does this for you.

    Thanks to Marty Borgen for his help debugging MathChip on PS/2 computers.

    Example:
         REM $INCLUDE: 'qlib.bi'
         msg$ = "No math coprocessor"
         IF MathChip THEN msg$ = "math coprocessor installed"
         PRINT msg$



 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

    Subroutine: MouseLimit(x0%, y0%, x1%, y1%)
    object file: mouse.obj

         MouseLimit confines the mouse's motion to an area limited by
    x0, y0, x1, y1.  Note that the x-dimension is horizontal and the
    y-dimension is vertical, and that both x and y are PIXELS, whether
    the video system is in graphics mode or text mode.

    Example:
         REM  keep the mouse out of the right side of the screen
         REM  assume SCREEN 12, 640 x 480 graphics
         x0% = 0: y0% = 0
         x1% = 600: y1% = 479
         CALL MouseLimit(x0%, y0%, x1%, y1%)



 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

    Subroutine: MousePos(x%, y%)
    object file: mouse.obj

         Positions the mouse cursor at (x,y).  Note that the x-dimension
    is horizontal and the y-dimension is vertical, and that both x and y
    are PIXELS, whether the video system is in graphics mode or text mode.

    Example:
         REM  put the mouse cursor in the upper left corner of the screen
         x% = 0:y% = 0
         CALL MousePos(x%, y%)


 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

    Function: buttons% = MouseReady
    object file: mouse.obj

         MouseReady determines if the Mouse driver software is loaded,
    and returns the number of mouse buttons if so.

    Example:
         REM $INCLUDE: 'qlib.bi'
         buttons% = MouseReady
         IF buttons% THEN PRINT buttons% + " button mouse installed"



 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

    Function: a$ = Path$(n%)
    object files: path.obj (strlen.obj, strncpy.obj)

    requires: DOS 3.xx or greater

    Path$() is a pseudo array which returns a path from the program's
    enviornment block.  If the length of the string returned by Path$
    is zero, there are no more paths in the enviornment block.

    Example:
         REM  the PATH statement in my AUTOEXEC.BAT file looks like this:
         REM  PATH=C:\;C:\MASM;C:\DOS;C:\F77L3;C:\OS386

         REM $INCLUDE 'qlib.bi'     ' tell BASIC about the function
         a$ = " ": n% = 0           ' initial conditions for WHILE/WEND
         WHILE LEN(a$) <> 0
         a$ = path$(n%)
         PRINT a$
         n% = n% + 1
         WEND

         REM  this prints:

         REM  C:\
         REM  C:\MASM
         REM  C:\DOS
         REM  C:\F77L3
         REM  C:\OS386





 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

     Subroutines: NumOFF, NumON
     object file: kbd2.obj

          Simplified controls to toggle the NumLock key.  See also
     GetKBDToggle and SetKBDToggle.

     Example:
          CALL NumON          ' this turns NumLock on



 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

    Function: PrinterError
    object file: prnerror.obj

        Determines whether the printer is ready.  PrinterError returns 0 if
    no error is detected.  If the printer is not turned on, or if it is out
    of paper, PrinterError returns -1.  On some printers, -1 is returned if
    the power is on but the printer is not on-line.

    Example:
         REM $INCLUDE 'qlib.bi'
         IF PrinterError THEN PRINT "Printer not ready or out of paper"



 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

    Subroutine: PrnScreenOFF
    Subroutine: PrnScreenON
    object file: prnscrn.obj

        These subroutines enable or disable the Print Screen key.

    Example:
        REM  disable Print Screen
        CALL PrnScreenOFF

        REM  turn it back on before ending the program
        CALL PrnScreenON

 



 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

     Subroutines: ScrollOFF, ScrollON
     object file: kbd2.obj

          Simplified controls to toggle the Scroll Lock key.  See also
     GetKBDToggle and SetKBDToggle.

     Example:
          CALL ScrollON       ' this turns Scroll Lock on




 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

    Subroutine: SetKBDToggle(kbd%)
    object file: kbd.obj

         Sets the NumLOCK, CapsLOCK, ScrollLOCK and INSERT keyboard toggles.
    See GetKBDToggle.

    Example:
         REM  let's be sure the NumLOCK toggle is ON and CapsLOCK is off
      REM  use the constants in GetKBDToggle

         CALL GetKBDToggle(kbd%)       ' get present toggles
         kbd% = (kbd% OR numb%)        ' this will set NumLOCK ON
         kbd% = (kbd% AND (NOT caps%)) ' clears CapsLOCK bit
         CALL SetKBDToggle(kbd%)



 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

    Subroutine: SetSpeed(speed%)
    object file: speed.obj

         Sets speed toggle of most "turbo" clone computers.  Speed% = 0 will
    set normal CPU speed, any other value for speed% will set "turbo" speed.
    Should not affect non-turbo computers (such as IBM PC, AT, etc.).  Good
    style suggests that before using this function for the first time, you
    should get the initial speed with GetSpeed and save it.  You should
    then restore the CPU to that original state before exiting the program.

    Example:
         CALL SetSpeed(speed%)