ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³    This Program brought to you through the facilities of        ³
      ³               ***  SIMPLE SOFTWARE COMPANY  ***                 ³
      ³                        P.O BOX 8184                             ³
      ³                    NEW ORLEANS, LA.  70182                      ³
      ³             >>>>>>>> Custom Programming <<<<<<<<                ³
      ³          Voice (504) 288-6550   Data (504) 283-9785             ³
      ³   Database - Accounting - Telecommunications - DOS Utilities    ³
      ³        Terry Tekippe, Ph.D, Gary M. Raymond, Programmers        ³
      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
                            by Gary M. Raymond

       Here is a summary of technical modem information collected from
       many sources over the past few years. Hopefully it will serve you
       as it has helped us. The information lacks great detail but has
       all the elemental information necessary for code writers.

       Standard IBM Default Values shown here.

       Vector Address = IRQ# plus 8

       PORT  DEC   HEX  ISR   VEC ADD   IRQ OCW1 MASK

       COM1  1016  3F8  IRQ4  12d(0xC)  AND 0xEF (or) AND (NOT 0x10)
       COM2  760   2F8  IRQ3  11d(0xB)  AND 0xF7 (or) AND (NOT 0x8)
       COM3  1000  3E8  IRQ4  12d(0xC)  AND 0xEF (or) AND (NOT 0x10)
       COM4  744   2E8  IRQ3  11d(0xB)  AND 0xF7 (or) AND (NOT 0x8)

       IRQ1  AND 0xFD  (various bit mask operations for OCW1 register
       IRQ2  AND 0xEF   depending on Interrupt Request Line in use)
       IRQ3  AND 0xF7
       IRQ4  AND 0xEF
       IRQ5  AND 0xDF
       IRQ6  AND 0xBF
       IRQ7  AND 0x7F

       NOTE: AT PC's may address many
             additional serial port
             addresses not mentioned here.


       REGISTER   (EXAMPLE: MCR for COM1 = 3F8+4 or 3FC)
       ---------------------------------------------
       IER  =  BASE  + 1  ;  Interrupt Enable Register
       IIR  =  BASE  + 2  ;  Interrupt Identification Register
       LCR  =  BASE  + 3  ;  Line Control Register
       MCR  =  BASE  + 4  ;  Modem Control Register
       LSR  =  BASE  + 5  ;  Line Status Register
       MSR  =  BASE  + 6  ;  Modem Status Register

       IER  BIT MAPPING
       ---------------------------------------------
       BIT     Activates             Action
       0    =  Data Received         Read RDR
       1    =  THR empty             Output to THR
       2    =  Data error/break      Read LSR
       3    =  MSR change            Read MSR
       4    =  zero
       5    =  zero
       6    =  zero
       7    =  zero

       IIR  BIT MAPPING
       ---------------------------------------------
       BIT
       0    =  more than 1 intr has occured
       1-2  =  00  change in MSR        10    data received
               01  THR empty            11    recv error/break
       3    =  zero
       4    =  zero
       5    =  zero
       6    =  zero
       7    =  zero

       LCR  BIT MAPPING
       ---------------------------------------------
       BIT
       0-1  =  Data Length      00=5bits           10=7bits
                                01=6bits           11=8bits
       2    =  Stop Bits        0=1bit             1=2bits
       3-5  =  Parity           000=Ignore         101=mark
                                100=ODD            111=space
                                110=EVEN
       6    =  Break Condition  0=disabled         1=enabled
       7    =  Port Toggle      0=Use THR/RDR/IER  1=Use BRDL/BRDH

       LSR  BIT MAPPING
       ---------------------------------------------
       BIT
       0    =  Set DTR line active
       1    =  Set RTS line active
       2    =  USER BIT #1
       3    =  USER BIT #2
       4    =  UART loopback
       5    =  zero
       6    =  zero
       7    =  zero

       LSR  BIT MAPPING
       ---------------------------------------------
       BIT
       0    =  byte in RDR (received)
       1    =  overrun in RDR
       2    =  Parity error detected
       3    =  Framing error (out of sync, no stop bit received)
       4    =  Break Detect
       5    =  THR empty
       6    =  TSR empty (removes char from THR)
       7    =  Time Out

       MSR  BIT MAPPING
       ---------------------------------------------
       BIT
       0    =  change in [C]lear [T]o [S]end  CTS
       1    =  change in [D]ata [S]et [R]eady DSR
       2    =  change in ring indicator RI
       3    =  change in [D]ata [C]arrier [D]etect  DCD
       4    =  Clear to send ..... [CTS] set high
       5    =  Data set ready .... [DSR] set high
       6    =  Ring Indicator .... [RI]  set high
       7    =  Data Carrier detect [DCD] set high
       ===================================================================
         
         AT        ATTENTION COMMAND
         A/        REPEAT COMMAND
         A         ANSWER MODE COMMAND
         B/B0      SELECT CCITT V.22 IN 1200 BPS
         B1        SELECT BELL 212A
         Dn        DIAL COMMAND (n = DIAL STRING, 0-9, *, #, !, W, R, AND,
         E         DISABLE ECHO
         E1        ENABLE ECHO 
         H         ON HOOK (HANG UP)
         H1        OFF HOOK
         I/I0      IDENTIFY
         I1        DISPLAY 000
         I2        DISPLAY OK
         I3        DISPLAY MESSAGE PROGRAM ROM
         L/L0      LOW VOLUME
         L1        LOW VOLUME
         L2        MEDIUM VOLUME
         L3        MAXIMUM SPEAKER VOLUME
         M/M0      DISABLE SPEAKER
         M1        SPEAKER ON UNTIL CARRIER
         M2        SPEAKER ALWAYS ON
         M3        DISABLE SPEAKER WHEN DIALING OR CARRIER
         O         GO ON LINE
         O1        RETRAIN (2400 BPS MODE ONLY)
         Q/Q0      ENABLE RESULT CODES
         Q1        DISABLE RESULT CODES
         Sn=X      S REGISTER WRITE (n = VALID S REG, X = ALLOWED VALUE SEE        
                   &F COMMAND)
         Sn?       READ SPECIFIED S REGISTER (n = ANY VALID S REGISTER)
         V0        SELECT DIGIT RESULT CODE
         V1        SELECT WORD RESULT CODE
         X0        BLIND DIAL, DISPLAY "CONNECT"
         X1        BLIND DIAL, DISPLAY "CONNECT 1200/2400"
         X2        DETECT DIAL TONE, DISPLAY "CONNECT 1200/2400"
         X3        DETECT BUSY TONE, DISPLAY "CONNECT 1200/2400"
         X4        DIAL AND BUSY TONE DETECT, DISPLAY "CONNECT 1200/2400"
         Y0        DISABLE LONG SPACE DISCONNECT
         Y1        ENABLE LONG SPACE DISCONNECT 
         Z         SOFTWARE RESET
         +++       ESCAPE CODE (GO TO COMMAND MODE IF ON LINE)
         &C0       DCD ALWAYS ON 
         &C1       DCD FOLLOWS REMOTE CARRIER STATUS
         &D0       IGNORE DTR
         &D1       GO TO COMMAND WHEN DTR ON TO OFF
         &D2       HANGUP AND GO TO COMMAND WHEN DTR ON TO OFF
         &D3       POWER UP RESET WHEN DTR ON TO OFF
         &F        FETCH FACTORY CONFIGURATION for S REGESTERS
         &G0       NO GUARD TONE 
         &G1       550 HZ GUARD TONE
         &G2       1800 HZ GUARD TONE 
         &J0       SELECT RJ-11/RJ-41S/RJ-45S
         &J1       SELECT RJ-12/RJ-13
         &M0       SELECT ASYNCHRONOUS MODE
         &P0       MAKE BREAK RATIO FOR US (40/60)
         &P1       MAKE BREAK RATIO FOR FOREIGN STANDARD (33/66)
         &R0       CTS TRACKS RTS
         &R1       CTS ON WHEN MODEM READY IN DATA MODE
         &S0       DSR ALWAYS ON
         &S1       DSR FOLLOWS RE232 SPECIFICATION
         &T0       STOP TEST 
         &T1       LOCAL ALB TEST
         &T3       LOCAL DLB
         &T        ENABLE DLB REQUEST
         &T5       DISABLE DLB REQUEST
         &T6       REMOTE DLB
         &T7       REMOTE DLB AND SELF TEST
         &T8       LOCAL ALB AND SELF TEST
         &V        VIEW PROFILE
         
         
         S-REG   ADDRESS  DEFAULT  VALID RANGE   DESCRIPTION
         
         S0      228      0        0-255         RING TO ANSWER ON
         S1      229      0        0-255         RING COUNT
         S2      230      43       0-127         ESCAPE CODE CHARACTER
         S3      231      13       0-127         CR CHARACTER
         S4      232      10       0-127         LF CHARACTER
         S5      233      8        0-127         BS CHARACTER
         S6      234      2        0-255         WAIT FOR DIAL TONE
         S7      235      30       1-30          WAIT FOR DATA CARRIER
         S8      236      2        0-255         PAUSE TIME FOR COMMA
         S9      237      6        1-255(.1SEC)  CARRIER DET RESP. TIME
         S10     238      14       1-255(.1SEC)  LOST CARRIER TO HANG UP        
                                                    DELAY
         S11     239                             TOUCH TONE DURATION
         S12     240      50       0-255         ESCAPE CODE GUARD TIME
                                    (1/50SEC)
         S13     241                             NOT USED
         S14     242      AAH                    BIT MAPPED OPTION REG
         S15     243                             NOT USED
         S16     244      0                      MODEM TEST OPTIONS
         S17     245                             NOT USED
         S18     246      0        0-255         TEST TIMER
         S19     247                             NOT USED
         S20     248                             NOT USED
         S21     249      0                      BIT MAPPED OPTIONS REG
         S22     250      76                     BIT MAPPED OPTIONS REG 
         S23     251      7                      BIT MAPPED OPTIONS REG
         S24     252                             NOT USED
         S25     253      5        0-255(.01SEC) DELAY TO DTR (SYNC ONLY)
         S26     254      1        0-255(.01SEC) RTS TO CTS DELAY (HALF                   
                                                    DUP)
         S27     255      40H                    BIT MAPPED OPTION REG
         
         
         
         RESULT CODES
         DIGIT     WORD            RESULT

         0         OK              Command executed without error.
         1         CONNECT         Carrier detected (300 bbs or 1200 bbs if      
                                      X0 is set.)
         2         RING            Phone is ringing (will answer only if    
                                      auto answer is enabled.)
         3         NO CARRIER      Carrier lost or never detected.
         4         ERROR           Error in command line, line too long, or 
                                      invalid character format.
         5         CONNECT 1200    Carrier detected at 1200 bbs if X1 set.
         6         NO DIALTONE     Displayed if no dialtone is detected        
                                      within 5 seconds and X2 or X4 is set.
         7         BUSY            Displayed when a busy signal is         
                                     detected and Z2 or X4 is set.
         8         NO ANSWER       Displayed when "@" dial modifier is used 
                                      and phone continues to ring.
         10        CONNECT 2400    Carrier detected at 2400 bbs. X1 or X2 
                                      must be set.
         

           MODEM          BELL 103    BELL 212    V.22        V.22 bis
           STANDARDS      300         1200        1200        2400
         
           BELL 300       300         300         300**       300**
         
           BELL 1200      1200*       1200        1200        1200
         
           CCITT 1200     1200*       1200        1200        1200
         
           CCITT 2400     2400*       1200        1200        2400
         
           CCITT 2400     300*        1200         1200         2400
         
         
         COMMAND             DESCRIPTION
         
         AT                  COMMAND LINE PREFIX (ATTENTION CODE);
                             PRECEDES COMMAND LINES EXCEPT +++ (ESCAPE)
                             AND A/ (REPEAT) COMMANDS.
         
         A/                 RE-EXECUTE LAST COMMAND LINE; (A/ IS NOT
                            FOLLOWED BY A CARRIAGE RETURN).
         
         A                  OFF-HOOK IN ANSWER MODE.
                                          5
         
         B                  SELECTS CCITT V.22 OPERATION WHEN 
                            COMMUNICATING AT 1200 BPS.
         
         B1  (Default)      SELECTS BELL 212A OPERATION WHEN
                            COMMUNICATING AT 1200 BPS.
         
         D                  DIAL NUMBER WHICH FOLLOWWD IN THE COMMAND
                            LINE.
         
         E                  MODEM DOES NOT "ECHO" COMMANDS BACK TO
                            TERMINAL.
         
         
         E1  (Default)      MODEM SECHOS COMMANDS BACK TO TERMINAL.
         
         H  (Default)       ON-HOOK (HANG-UP) COMMAND.
         
         H1                 GO OFF-HOOK.
         
         I                  REQUEST PRODUCT IDENTIFICATION CODE.
         
         I1                 PERFORMS CHECKSUM ON FIRMWARE ROM; RETURNS
                            CHECKSUM.
         
         I2                 PERFORMS CHECKSUM ON FIRMWARE ROM; RETURNS
                            OK OR ERROR.
         
         M                  SPEAKER OFF.
         
         M1  (Default)      SPEAKER ON UNTIL CARRIER DETECTED.
         
         M2                 SPEAKER ALWAYS ON.
         
         M3                 SPEAKER ON UNTIL CARRIER DETECTED EXCEPT
                            DURING DIALING.
         
         O                  RETURN TO ON-LINE STATE.
         
         O1                 RETURN TO ON-LINE STATE AND INITIATE RETRAIN.
         
         Q  (Default)       MODEM RETURNS RESULT CODES.
         
         Q1                 MODEM DOES NOT RETURN RESULT CODES.
         
         SRT=N              SET REGISTER R TO VALUE N.
         
         SR?                REQUEST CONTENTS OF REGISTER R.
         
         
         V                  SHORT FORM NUMERIC RESULT CODES.
         
         V1  (Default)      FULL WORD RESULT CODES.
         
         X                  300 BPS COMPATIBILITY MODE; CONNECT RESULT
                                          6
                            CODE ENABLED.
         
         X1                 MODEM BLIND DIALS; ALL CONNECT XXXX RESULT
                            CODES ENABLED; BUSY SIGNAL NOT DETECTED.
         
         
         X2                 MODEM WAITS FOR DIAL TONE BEFORE DIALING;
                            ALL CONNECT XXXX RESULT CODES ENABLED; MODEM
                            SEND BUSY RESULT CODE IF BUSY DETECTED.
         
         X3                 MODEM BLIND DIALS; ALL CONNECT XXXX RESULT
                            CODES ENABLED; MODEM SENDS BUSY CODE IF BUSY
                            DETECTED.
         
         X4  (Default)      MODEM WAITS FOR DIAL TONE BEFORE DIALING;
                            ALL CONNECT XXXX RESULT CODES ENABLED; BUSY
                            SIGNAL DETECTED.
         
         Z                  LOAD STORED CONFIGURATION PROFILE.
         
         &C                 DCD ALWAYS ON.
         
         &C1  (Default)     DCD ON INDICATES PRESENCE OF DATA CARRIER.
         
         &D   (Default)     MODEM IGNORES DTR.
         
         &D1                MODEM ASSUMES COMMAND STATE WHEN ON-TO-OFF
                            TRANSITION DETECTED ON DTR.
         
         &D2                MODEM HANGS UP & ASSUMES COMMAND STATE.
                            AUTO ANSWER NOT DISABLED UNLESS EXTERNALLY
                            IMPLEMENTED BY (RI- # DTR-)= A6-.
         
         &D3                MODEM ASSUMES INITIALIZATION STATE UPON
                            DETECTING AN ON-TO-OFF TRANSITION ON DTR.
         
         &F                 LOAD FACTORY CONFIGURATION PROFILE.
         
         &P  (Default)      PULSE DIAL MAKE/BREAK RATIO = 39/61 (UK/HK).
         
         &P1                PULSE DIAL MAKE/BREAK RATIO = 33/67 (UK/HK).
         
         &S                 DSR ALWAYS ON.
         
         &S1                DSR OPERATES IN ACCORDANCE WITH EIA RS-232-C
                            SPEC.
         
         &T                 TERMINATE TEST PROGRESS.
         
         &T1                INITIATE LOCAL ANALOG LOOPBACK TEST.
         
         &T8                INITIATE LOCAL ANALOG LOOPBACK WITH SELF TEST.
         
         &Z                 STORE TELEPHONE NUMBER.
         

         EXPLANATIONS
         
         A     Go off hook and answer phone immediately. The Model 2400 
               immediately goes off hook, transmits the answer tone and 
               waits for a carrier from the remote mode.
               Commands entered after the A command are ignored.
         
         A/    Repeat previous command. The last command executed by the 
               Model 2400 will execute again. This command does not require
               the "AT" prefix or <cr> termination.
         
         Bn    Bell/CCITT mode select.
         
               B0 - Selects CCITT V. 22 operation at 1200 bps.
               B1 - Selects BELL212A operation at 1200 bps (Default).
         
               Most 1200 bps modems in the United States operate using the 
               BELL212A specification. In order to communicate with a modem
               conforming to the international CCITT V.22 standard, issue
               the B0 command before dialing.
         
         Dn    Dial the number immediately following this command where
               n = digits 0 through 9 together with the dial modifiers 
               listed below.
         
               Dial Modifiers:  P  Pulse dial
                                T  Tone dial
                                R  Originate call in answer mode
                                W  Wait for dial tone before dialing
                                ,  Pause before dialing next digit
                                ;  Return to command mode after dialing
                                @  Wait for quiet answer before dialing
                                !  Flash-hook
                                S  Dial the number stores in RAM
         
         DIAL MODIFIERS
         
         P                   PULSE DIAL
         
         T                   TONE DIAL
         
         ,                   PAUSE
         
         !                   FLASH
         
         @                   WAIT FOR SILENCE
         
         W                   WAIT FOR SECOND DIAL TONE
         
         ;                   RETURN TO COMMAND STATE AFTER DIALING
         
         R                   ORIGINATE CALL IN ANSWER MODE
         
         D                   DIAL STORED NUMBER
         

ALL S REGISTER COMMANDS ARE ENTERED IN THE AT COMMAND LINE.
EXAMPLE: AT S8=2 S2=43 S7=30
TO READ THE VALUE IN ANY REGISTER USE
         AT S#? <CR>
THE MODEM SHOULD ECHO THE VALUE FOUND IN THE REGISTER #

REG  Values      Register function
S0   0           AUTO ANSWER OFF
     1-255       AUTO ANSWER ON, ANSWER ON INDICATED # OF RINGS
S1 **0-255       RING COUNT (THIS IS A READ-ONLY REGISTER)
S2   0-127       ESCAPE CHARACTER  NORMALLY SET TO 43 OR "+"
     127-255     ESCAPE FUNCTION DISABLED
S3  0-127        END OF LINE CHARACTER  NORMALLY SET TO 13 (CR)
S4  0-127        LINE FEED CHARACTER  NORMALLY SET TO 10 (LF)
S5  0-127        BACKSPACE CHARACTER  NORMALLY SET TO 8 (BS)
S6  2-255  SEC   PAUSE BEFORE DIALING (NORMALLY 2 SEC)
S7  1-255  SEC   WAIT FOR CARRIER (NORMALLY SET TO 30 SEC)
S8  0-255  SEC   PAUSE FOR COMMA IN DIAL STRING (NORMALLY SET TO 2 SEC)
S9  1-255  .1SEC CARRIER VALIDATION TIME NORMALLY 6 (.6 SEC)
S10 1-255  .1SEC LOSS OF CARRIER DISCONNECT DELAY NORMALLY 14 (1.4 SEC)
S11 50-127 .1SEC TOUCH TONE DURATION. THE DEFAULT IS 90.
S12 20-255 .02SE ESCAPE SEQENCE PAUSE  NORMALLY 50 (1.0 SEC)
S13 *            POWER UP ASYNC DATA FORMAT (USE CHART BELOW)
S14 *            OPTION STATUS DEFULT AA (HEX CODE) (USE CHART BELOW)
S16 *            DEFULT 0. TEST STATUS (USE CHART BELOW)
S18 0-255 SEC    DEFULT 0. TEST TIMER (REMOTE TEST)
S21 *            DEFULT 0.OPTION STATUS  (USE CHART BELOW)
S22 *            OPTION STATUS, DEFULT 76. (USE CHART BELOW)
S23 *            OPTION STATUS  NORMALLY 07 (USE CHART BELOW)
S25 0-255 SEC    DTR DETECT DELAY NORMALLY 5 SEC
                 ASYNC MODE, SYIC AUTO-DIAL AND SYIC MANUAL DIAL MODE .05 SEC
S26 0-255 MS     RTS TO CTS DELAY (1 MS)
S27 *            OPTION STATUS, DEFULT 40 (HEX CODE)  (USE CHART BELOW)

* REGISTERS USED BY MODEM PROCESSOR. DO NOT ALTER THESE
* READ ONLY REGISTERS

S13 DATA FORMAT:

POSITION  VALUE  FUNCTION
 BIT 0      -    NOT USED
 BIT 1      -    NOT USED
 BIT 2      0    PARITY OFF
            1    PARITY ON
 BIT 3      0    ODD PARITY
            1    EVEN PARITY
 BIT 4      0    7 DATA BITS
            1    8 DATA BITS
 BIT 5      0    BIT 8=0
            1    BIT 8=1
 BIT 6      -    NOT USED
 BIT 7      -    NOT USED

S14 DATA FORMAT:
 BIT 0      -    NOT USED
 BIT 1      0    LOCAL CHARACTER ECHO OFF
            1    LOCAL CHARACTER ECHO ON
 BIT 2      0    STATUS DISPLAYS ON
            1    STATUS DISPLAYS OFF
 BIT 3      0    STATUS CODES SENT
            1    STATUS MESSAGES SENT
 BIT 4      0    MODEM RESPONDS TO COMMANDS
            1    MODEM IGNORES COMMANDS
 BIT 5      0    TONE-DIALING
            1    PULSE-DIALING
 BIT 6      -    NOT USED
 BIT 7      0    ANSWER MODE
            1    ORIGINATE MODE

S16 DATA FORMAT:
 BIT 0      0    ANALOG LOOP OFF
            1    ANALOG LOOP ACTIVE
 BIT 1      -    NOT USED
 BIT 2      0    DIGITAL LOOP OFF
            1    DIGITAL LOOP ACTIVE
 BIT 3      0    REMOTE DIGITAL LOOP REQUESTED BY OTHER MODEM IS OFF
            1    REMOTE DIGITAL LOOP REQUESTED BY OTHER MODEM IS ACTIVE
 BIT 4      0    REMOTE DIGITAL LOOP OFF
            1    REMOTE DIGITAL LOOP ACTIVE
 BIT 5      0    SELF TEST RDL OFF
            1    SELF TEST RDL ACTIVE
 BIT 6      0    SELF TEST ANALOG LOOP OFF
            1    SELF TEST ANALOG LOOP ACTIVE
 BIT 7      -    NOT USED

S21 DATA FORMAT:
 BIT 0      0    RJ11/RJ41/45 JACK TYPE
            1    RJ12/FJ13 JACK TYPE
 BIT 1      -    NOT USED
 BIT 2      0    CTS FOLLOWS RTS
            1    CTS FORCED ON
 BIT 3&4    0    MODEM IGNORES DTR
            1    MODEM ASSUMES COMMAND STATE WHEN DTR TURNS OFF
            2    MODEM ASSUMES COMMAND STATE AND DISABLES AUTO-ANSWER
                 WHEN DTR TURNS OFF
            3    MODEM RESETS WHEN DTR TURNS OFF
 BIT 5      0    DCD FORCED ON
            1    DCD FOLLOWS CARRIER
 BIT 6      0    DSR FORCED ON
            1    DSR BEHAVES NORMALLY
 BIT 7      0    LONG SPACE DISCONNECT DISABLED
            1    LONG SPACE DISCONNECT ENABLED

S22 DATA FORMAT:
 BIT 0&1    1    LOW SPEAKER VOLUME
            2    MEDIUM SPEAKER VOLUME
            3    HIGH SPEAKER VOLUME
 BIT 2&3    0    SPEAKER ALWAYS OFF
            1    SPEAKER ON UNTIL CARRIER DETECTED
            2    SPEAKER ALWAYS ON
            3    SPEAKER OFF DURING DIALING THEN ON UNTIL CARRIER DETECTED
 BIT 4&5&6  0    X COMMAND IN EFFECT
            4    X 1 COMMAND IN EFFECT
            5    X 2 COMMAND IN EFFECT
            6    X 3 COMMAND IN EFFECT
            7    X 4 COMMAND IN EFFECT
 BIT 7      0    39/61 MAKE/BREAK RATIO (PULSE DIALING)
            1    33/67 MAKE/BREAK RATIO

S23 DATA FORMAT:
 BIT 0      0    REMOTE DIGITAL LOOP REQUEST DENIED
            1    REMOTE DIGITAL LOOP REQUEST GRANTED
 BIT 1&2    0    0-300 BPS
            1    600 BPS
            2    1200 BPS
            3    2400 BPS
 BIT 3      -    NOT USED
 BIT 4&5    0    EVEN PARITY
            1    PARITY BIT ALWAYS 0
            2    ODD PARITY
            3    PARITY BIT ALWAYS 1
 BIT 6&7    0    NO GUARD TONES
            1    550 HZ GUARD TONE
            2    1800 HZ GUARD TONE

S27 DATA FORMAT:
 BIT 0&1    0    ASYNCRONOUS MODE
            1    ASYNC/SYNC MODE
            2    SYNC AUTO-DIAL
            3    SYNC MANUAL DIAL
 BIT 2      0    PUBLIC PHONE LINE
            1    LEASED LINE
 BIT 3      -    NOT USED
 BIT 4&5    0    INTERNAL CLOCK USED
            1    EXTERNAL CLOCK USED
            2    SLAVED CLOCK USED
 BIT 6      0    CCITT V.22 PROTOCOL (1200 BPS)
            1    BELL 212A (1200 BPS)
 BIT 7      -    NOT USED


OTHER MODEM COMMANDS:

AT       STANDARD LEAD IN SEQUENCE (ATTENTION)
ATA      FORCE ANSWER
ATD      DIAL (ATD ###-#####)
   P     PULSE (ATDP ###-####)
   T     TONE  (ATDT ###-####)
ATE1     ENABLE LOCAL CHARACTER ECHO
ATE0     DISABLE LOCAL CHARACTER ECHO
ATH1     FORCE LINE CONNECT
ATH0     FORCE LINE DISCONNECT
ATI      ECHO VERSION TYPE
ATL1     SPEAKER VOLUME LOW
ATL2     SPEAKER VOLUME MEDIUM
ATL3     SPEAKER VOLUME HIGH
ATM0     SPEAKER ALWAYS OFF
ATM1     SPEAKER ON EXCEPT WHILE CARRIER PRESENT
ATM2     SPEAKER ALWAYS ON
ATM3     SPEAKER ON EXCEPT WHILE DIALING AND CARRIER PRESENT
ATO      GO ONLINE AFTER ESCAPE OR WHILE IN COMMAND MODE
ATQ0     STATUS DISPLAY ON
ATQ1     STATUS DISPLAY OFF
ATV0     STATUS MESSAGES SENT
ATV1     STATUS CODES SENT
ATX0     "CONNECT" (CODE 1)  ALL SPEEDS NO DIAL TONE DETECTION
ATX1     "CONNECT" (CODE 1)  0-300 BPS OR "CONNECT 1200" FOR 1200 OR
         "CONNECT 2400" FOR 2400 BPS NO DIAL TONE DETECTION
ATX2     WAIT FOR DIAL TONE (CONNECT SPEEDS SHOWN AS FOR X1)
ATX3     DETECT BUSY SIGNAL (CONNECT SPEEDS SHOWS AS FOR X1)
ATX4     WAIT FOR DIAL TONE, DETECT BUSY SIGNAL (CONNECT SPEEDS SHOWS AS FOR X1)

ATZ      RESET TO POWER UP CONDITION (CLEARS ALL REGISTERS)



2400 MODEM SPECIAL COMMANDS:    (* = FACTORY SETTING STANDARD)

ATB0     CCITT V.22 AT 1200 BPS
ATB1     BELL 212A AT 1200 BPS *

AT &F    RESTORE TO FACTORY C0NFIGURATION
AT &G    NO GUARD TONE *
AT &G1   550 HZ GUARD TONE
AT &G2   1800 HZ GUARD TONE
AT &J    RJ11/RJ41S/RJ45 JACK *
AT &J2   RJ12/RJ13 JACK
AT &L    REGULAR PHONE LINE *
AT &L1   LEASED LINE
AT &M    ASYNC OPERATION *
AT &M1   ASYNC/SYNC OPERATION
AT &M2   SYNC AUTO DIAL
AT &M3   SYNC MANUAL DIAL
AT &P    39/61 PULSE MAKE/BREAK RATIO *
AT &P1   33/67 PULSE MAKE/BREAK RATIO
AT &T4   GRANT RDL TEST REQUEST *
AT &T5   DENY RDL TEST REQUEST
AT &V    VIEW STATUS OF ALL MODEM SETTINGS. SEE ALL S REGISTER SETTINGS AND
         INTERNAL MODEM COMMAND SETTINGS ON ONE SCREEN!
AT &X    SYNC CLOCK INTERNAL *
AT &X1   SYNC CLOCK EXTERNAL
AT &X2   SYNC CLOCK SLAVED
AT &Z    STORE DIAL COMMAND LINE

DATA INTERFACE (2400)
AT &C    DCD ALWAYS ON 
AT &C1   DCD ON WHILE CARRIER PRESENT *
AT &D    DTR IGNORED *
AT &D1   DTR FAIL DISCONNECT ENABLED (MODEM RETURNS TO COMMAND MODE)
AT &D2   DTR FAIL DISCONNECT ENABLED (MODEM RETURNS TO COMMAND MODE, TURN
         AUTO ANSWER OFF)
AT &D3   DTR FAIL DISCONNECT ENABLED (RESET MODEM)


                                EOF()