TeleReplica Instruction Manual

0.    To Get TeleReplica Up and Running Quickly...

      If you will be using modems then read the modem setup suggestions at the
      start of appendix A. Then read whichever of the following sections most
      closely matches your own application:
         A1  Consultant/Client via Modem
             One consultant wishing to connect via modem to many different
             clients in order to take over the clients' computers.
         A2  Remote/Shared via Modem
             One remote access PC to be taken over by many different users via
             modem.
         A3  Laptop/Desktop via Direct Cable
             A simple direct connection with no modems.
         A4  Remote/Shared via Common Mini-computer
             Instead of a direct link between the two PCs, each PC will be
             logged into a common UNIX system.
         A5  Home/Office via Modem
             A dedicated office PC to be taken over from a home PC.


1.    What TeleReplica Will Do

1.1   TeleReplica will allow you to connect two IBM PC-compatible computers
      together (via telephone lines and modems, or via a direct cable, or via a
      common mini- or main-frame computer), and arrange for input to be
      accepted from either keyboard, and for both displays to appear identical.
      In this document the computer which is running normal programs is called
      the host computer, and the other computer is called the replica computer,
      since its display is a replica of the host computer's display.

1.2   TeleReplica will do a reasonable job of optimizing the screen changes
      transmitted, so that (for example) moving a highlighted menu bar will
      appear almost immediately even at 1200 bps (provided the call is
      relatively local).

1.3   TeleReplica always updates the replica computer's screen to match the
      current host screen. This means that if several commands are issued
      without waiting for the display to catch up, then the replica screen will
      be updated to show the final host screen, without wasting time
      transmitting the intermediate screens.

1.4   TeleReplica uses a password of up to 39 characters, which means an
      intruder would (on average) take millions of years at 2400 bps to guess a
      well chosen password! Since this password is transmitted automatically,
      there is no need to keep it short and easy to remember - once TeleReplica
      is installed, you will never need to enter the password manually.

1.5   TeleReplica will allow the host site to call the replica site, or the
      other way around. For consultants this means you can make your clients
      pay the 'phone bills!

1.6   TeleReplica will automatically detect the "baud" rate being used by the
      replica computer, and set the host computer's "baud" rate to match. This
      means that users with different speed modems can all access a single
      host.

1.7   TeleReplica uses less than 10K of memory on the host computer, which
      means there should be enough memory left to run most applications.

1.8   TeleReplica can be installed to "type" a command in response to the
      'phone ringing, which allows better control than merely using the modem's
      auto-answer capability. It can also send a command directly to the modem.

1.9   TeleReplica will trap anything printed to any printer on the host PC, and
      redirect it to the chosen printer at the replica PC. This redirection
      takes place only when a session is active, so at other times the host can
      be used to print normally even if TRHOST is still loaded.

1.10  TeleReplica will allow the host PC to run with screen blanked and
      keyboard dead for improved privacy.

1.11  TeleReplica will support file transfers using external protocol programs
      such as DSZ, which provide crash recovery and cope better with poor lines
      than TeleReplica's built-in protocol.

1.12  TR is "DESQview-Aware". See Appendix D for details.

1.13  Full source code is available at a small cost. See REGISTER.DOC for
      details.


2.    What TeleReplica Will NOT Do

2.1   TeleReplica will not replicate graphics displays. If the user at the
      replica computer runs a program that displays graphics, then the replica
      display may show (textual) garbage. Keystrokes will still be transmitted
      to the host computer, but the user must remember which keys are necessary
      to get out of graphics mode again! TeleReplica gives a warning that
      graphics mode has been entered, but by then it is too late to avoid it.
      However, in an emergency TR can instruct the host computer to reboot, so
      provided TRHOST is run from AUTOEXEC.BAT this provides a means of
      recovery.

2.2   TeleReplica will only replicate text page 0, and only as an 80 column by
      25 line display.

2.3   TeleReplica will only work with the standard keyboard buffer (starting at
      the address in segment 0040h specified at offset 0080h, ending at the
      address specified at offset 0082h, with head pointer stored at offset
      001Ah, and tail pointer stored at offset 001Ch).

2.4   Where TeleReplica is being used with a modem, it will work best if the
      modem and modem cable provide carrier detect, data terminal ready and
      ring indicator signals in addition to the minimum transmit data, receive
      data and ground signals.

2.5   TeleReplica will cause bad "snowing" on some older CGA display cards. No
      attempt has been made to use the retrace intervals for screen memory
      access.

2.6   TeleReplica will slow down the normal operation of the host computer. On
      a 4.77MHz PC performance can be halved; on a faster host the difference
      will not be so noticeable.

2.7   TeleReplica requires DOS 3.0 or later.

2.8   TeleReplica will not work particularly well on a noisy 'phone line. File
      transfers are error-checked, but normal screen updates are not. Normally
      this will not be a problem, since a corrupted screen will be obvious to
      the user and in any case TR will usually detect the problem and
      automatically request a full refresh. However, if errors happen very
      frequently then TR can spend all its time continually re-refreshing the
      display! Printer capture also is not error-checked, so line noise will
      garble the printout.


3.    Why Use TeleReplica?

3.1   Access to Local Area Network from Home

      TeleReplica will allow you to connect into your office computer from
      home. This means you do not need to take all your data files home with
      you, and that you do not need to license additional copies of your
      software (since your home computer is not running the software, only
      replicating the screen of your office computer). If your office computer
      is part of a local area network, then you automatically have access to
      all the network facilities from home.

      We regularly use TeleReplica with such programs as WordPerfect,
      WordPerfect Office (especially mail), WordStar, FoxBASE, Lotus-style
      spreadsheets, all the Novell NetWare utilities, and our local area
      network is regularly backed up after hours via TeleReplica! The only
      programs we have come across that could not be used remotely either:
         a) used graphics displays (e.g. WordPerfect preview); or
         b) took over interrupts needed by TRHOST (e.g. comms programs); or
         c) used text pages other than 0 (e.g. Turbo Debugger?)

3.2   Software Support

      TeleReplica will allow you to take over your client's computer, so that
      you can see what is going wrong. In many cases this will avoid the need
      for an expensive trip to the client's site.

      For details of these and other applications, see the scenarios in
      Appendix A.


4.    TeleReplica Host Installation

      To install TeleReplica at the host computer, first copy the files:
      TRHOSTIN.EXE, TRHOSTC.EXE, TRHOST.EXE, TRPUT.EXE, TRGET.EXE, TRTALK.EXE,
      TRCHECK.EXE, TRASK.EXE, TRDIAL.EXE, TREXTR.EXE, TREXTS.EXE, TRMODSET.EXE,
      TRRZ.BAT and TRSZ.BAT into a directory (say \TR) on the host computer.
      Then enter the command:
         TRHOSTIN

      Your display should show a menu similar to:
      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º TeleReplica Host 3.20 Installation Copyright (c) 1992 Douglas Thomson º
      º                                                                       º
      º    A. Select serial port (currently COM1)                             º
      º    B. Change password (currently "password")                          º
      º    C. Change modem initialization string (currently:                  º
      º       "\rat &c1 &d2\r")                                               º
      º    D. Change modem dialing format string (currently:                  º
      º       "atdt %s\r")                                                    º
      º    E. Select maximum "baud" rate (currently 2400)                     º
      º    F. Use modem CARRIER DETECT signal (currently YES)                 º
      º    G. Flow control (currently NONE)                                   º
      º    H. Generate INT 9 on each key (currently NO)                       º
      º    I. Respond to modem RING signal (currently NO)                     º
      º    J. Reboot on loss of carrier (currently NO)                        º
      º    K. Synchronize "baud" rate (currently YES)                         º
      º    L. Send wakeup every 2 minutes (currently NO)                      º
      º    M. Private mode (currently NO)                                     º
      º    N. Printer redirection (currently HOST)                            º
      º    O. Create consistent .TR file                                      º
      º    Q. Abandon changes                                                 º
      º    S. Save changes and leave installation program                     º
      º                                                                       º
      º Selection:                                                            º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
      Consider each of these options in turn:

4.1   Select Serial Port

      Another menu will appear:
      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º TeleReplica Host Program Serial Port Selection           º
      º                                                          º
      º    0. Completed, no (further) change                     º
      º => 1. COM1 port (base 0x03F8, interrupt IRQ4)            º
      º    2. COM2 port (base 0x02F8, interrupt IRQ3)            º
      º    3. COM3 port (base 0x0000, interrupt IRQ4)            º
      º    4. COM4 port (base 0x0000, interrupt IRQ3)            º
      º    A. Custom base (currently 0x03F8)                     º
      º    B. Custom interrupt (currently IRQ4)                  º
      º                                                          º
      º Selection:                                               º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
      All four "standard" ports are listed, although the port addresses for
      non-existent ports are unlikely to be meaningful (if you are lucky, they
      will be flagged with a base of 0x0000). To select one of these ports,
      just type the port number. If you have a non-standard port/interrupt
      combination, then use A and B to specify exactly what you want. When you
      are happy with the settings, select 0 to return to the main menu.

      Please note that I do not have access to any system which uses the AT IRQ
      numbers (8-15), so I cannot guarantee the performance of TeleReplica when
      these 16-bit cards are used. Also, since COM1 and COM3 share the same
      interrupt, only one or other of these ports can be in use at the same
      time (the same applies to COM2 and COM4).

4.2   Change Password

      The string editing menu will appear:
      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º TeleReplica Host Program Password Selection                           º
      º                                                                       º
      º Edit existing string:                                                 º
      º password                                                              º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
      Whenever you see the "Edit existing string:" prompt, you can use the left
      and right arrow keys to move the cursor through the string, and the
      backspace and delete keys to delete characters to the left of or under
      the cursor respectively. Any normal characters you type will be inserted
      at the cursor position. If the first key you press is a normal printable
      character then the string will be cleared automatically.

      You will not be able to enter more than the maximum allowed number of
      characters for any string.

      Since you will only need to enter the password once during installation,
      and never in normal use, it is recommended that you make the password
      near the maximum length and quite random. The main thing is that no-one
      should have any chance of guessing the password.

4.3   Change Modem Initialization String

      The string editing menu will appear again, this time asking for the modem
      initialization string. This string is transmitted to the modem at the
      maximum "baud" rate when TRHOST runs for the first time. If you are using
      an automatic power switch that powers up the host computer when the
      'phone starts ringing, then the initialization string may need to answer
      the 'phone (see scenario A2). There may also be various operating modes
      that cannot be stored permanently in your modem's non-volatile memory,
      and which must therefore be established each time TRHOST starts. In many
      applications, where nothing needs to be changed, this string may be
      empty.

      You will probably need to refer to the instruction manual for the host
      modem to work out what if anything is required.

      As well as normal characters, you may need to include some special
      characters such as carriage return. Carriage return can be encoded as \r
      (see the main menu at the start of section 4). Alternatively, any
      character can be entered in hexadecimal as \0x followed by two hex digits
      (for example, the escape key is \0x1B).

      It may also be necessary to include some kind of delay. For example, some
      modems go off into a world of their own for a second or so after a reset
      command. Delays are entered in milliseconds as \D followed by the delay
      (for example, \D1000. [1 second] or \D500. [half a second]). Delays are
      only accurate to the nearest 1/18.2th of a second, so the number you
      enter may be modified slightly to reflect the nearest possible actual
      delay.

4.4   Change Modem Dialing Format String

      This string determines what TRDIAL will send to the modem to dial a
      number. The usual use of TRDIAL will be something like TRDIAL 221166, so
      normally the dialing format string should contain a %s to insert the
      number. For example, if the dialing string is "atdt %s\r" and the user
      enters the previous dialing command, then what will be sent to the modem
      is "atdt 221166\r".

      Alternatively, if only one number is required, then the dialing format
      string may contain the actual number, in which case the user will only
      need to enter TRDIAL by itself.

      Note that (when CARRIER DETECT is being used) TRDIAL will only send
      anything to the modem if there is NO carrier detected - once a carrier
      had been established the modem would not act on the command in any case,
      but would send it through to the other end. When TRHOST is installed to
      ignore CARRIER DETECT, TRDIAL will send data to the modem regardless.

4.5   Select Maximum "Baud" Rate

      Another window will appear:
      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º TeleReplica Host Program Maximum "Baud" Rate Selection                º
      º                                                                       º
      º Enter "baud" rate:                                                    º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
      You should enter the maximum "baud" rate that the host modem is capable
      of using. Usually this will be 1200, 2400 or 9600. Note that TRHOST can
      automatically adjust to half this speed, a quarter of this speed, or one
      eighth of this speed. Thus if you choose 9600 bps, TRHOST will be able to
      work at 9600, 4800, 2400 or 1200 bps (provided the host modem can handle
      these speeds).

      If you will be using a direct cable between two PCs, then 19200 should
      work on all systems and 38400 will work on faster computers. If your
      computers have NS16550AFN UART chips instead of the standard 8250 chips
      then you may find speeds of 57600 or even 115200 work even on slower PCs
      (not tested, I only have the 8250!).

4.6   Use modem CARRIER DETECT signal

      Selecting this option will determine whether or not TRHOST will use the
      carrier detect signal provided by the modem. If you are using a real
      modem, then you should set this to YES and make sure the modem is
      initialized so that it reports the true CD status from the 'phone line.

      If you are using a direct cable between two PCs, or connecting PCs via a
      mini-computer, then set this option to NO.

4.7   Flow control

      Selecting this option will bring up the following menu:
      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º TeleReplica Host Program Flow Control Selection          º
      º                                                          º
      º    0. Completed, no (further) change                     º
      º => 1. No flow control                                    º
      º    2. Hardware (RTS/CTS) flow control                    º
      º    3. Software (XON/XOFF) flow control                   º
      º    4. Both hardware and software flow control            º
      º    5. Set inter-character gap time (currently 330 ms)    º
      º                                                          º
      º Selection:                                               º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

4.7.1 TeleReplica can use the following flow control systems:
      NONE     No flow control. Use this with a direct cable or with modems
               that require no speed adjustment.
      CTS      Hardware flow control using RTS (request to send) and CTS (clear
               to send). Use this in preference to software flow control if it
               is available.
      XON      Software flow control using XON and XOFF (^S/^Q). Use this if
               flow control is needed and hardware flow control is not
               available.
      BOTH     Use both software and hardware flow control. I can't imagine why
               anyone would want this...

4.7.2 Normally TeleReplica will not need to use any flow control even when it
      is available. However, some modems communicate with the PC at a different
      speed than that at which they communicate with other modems, so that it
      is possible for the PC to "get ahead" of the modem and hence lose data.
      In these cases it is necessary for the modem to tell the PC when to wait
      a bit before sending the next byte.

4.7.3 A side effect of software flow control is that TeleReplica will not use
      ANY control characters: it will not send any, and it will ignore all
      control characters received apart from XON and XOFF. This may be useful
      for networks that respond to certain control characters; however, binary
      file transfers will be slightly slower since 64 characters (control
      characters with and without the parity bit) are not used. Note that both
      TR and TRHOST must therefore either use or not use software flow control
      - if one end uses software flow control and the other does not, then no
      communication will be possible!

4.7.4 When TRHOST is receiving characters (normally keys that have been pressed
      at the remote PC - each key is encoded as two or three characters) it
      waits a certain length of time after receiving the first character before
      giving up and ignoring the key. This is important, since otherwise a
      single byte introduced by noise on the line could cause all subsequent
      keys to be misinterpreted (the second character of one key being treated
      as the first character in the next key and so on). TR always sends all
      the characters which constitute one key as close together as the
      communication speed will allow, so usually a gap of even 0.1 seconds
      means that something has gone wrong and that TRHOST should start looking
      for a new key again. However, if the link between TR and TRHOST uses
      packets, or for any other reason introduces significant gaps between two
      characters that were sent together, then TRHOST may need to be adjusted
      to tolerate longer gaps between characters which should be together.
      Selecting option 5 will bring up the following screen:
      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º TeleReplica Host Program Inter-character Gap Time Selection           º
      º                                                                       º
      º Longest gap to be tolerated (ms): 330                                 º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
      Any time up to about 10 seconds (10000 ms) can be entered. Be aware that
      if this time is set to 10 seconds, and line noise does introduce a stray
      character, then you will need to wait 10 seconds without typing anything
      at the remote PC to get TRHOST back into synchronization!

4.8   Generate INT 9 on each key

      When TRHOST receives a key from TR, it will usually just place it in the
      keyboard buffer to be found by any program that wants to read a key.
      However, some applications monitor the keyboard interrupt (INT 9) and
      only read the keyboard input buffer after there has been a keyboard
      interrupt! To keep such programs happy, TRHOST can generate an INT 9
      after it has placed a key into the buffer. However, this can cause
      problems for other programs, particularly when the host and remote
      keyboards may both be in use at the same time (e.g. TRTALK). Leave this
      option OFF unless it is really necessary.

4.9   Respond to modem RING signal

      Selecting this option will determine whether or not TRHOST will respond
      to the RING signal which the modem provides to tell the PC that the
      'phone is ringing. If this option is turned on, then the menu will be
      extended with the following sub-options:

      G. Respond to modem RING signal (currently YES)ÄÄÄÂÄ 1. too short  220 ms
                                                        ÃÄ 2. too long  5000 ms
                                                        ÃÄ 3. delay    10000 ms
                                                        ÃÄ 4. reset    10000 ms
                                                        ÃÄ 5. "type" response
                                                        ÀÄ 6. response Ä¿
                                                                "\0x1Btrauto\r"

4.9.1 If the 'phone only rings for a very short time, you may wish to ignore
      the ringing completely - otherwise just knocking the 'phone off the hook
      can trigger a TRHOST response!

4.9.2 If the 'phone rings for a long time, then this may indicate that the
      caller is a person who should not be greeted by an ear full of modem! If
      TRHOST is intended to respond before the 'phone stops ringing, then this
      time should be set the same as the delay below.

4.9.3 After a certain length of time (measured from when the 'phone starts
      ringing) TR will check that the amount of ringing was within the
      specified range, and if so, will "type" the response string (see point
      5).

4.9.4 If the 'phone rang for too long, then TR must know when to start looking
      for another call. If the 'phone has not rung for a certain length of time
      then TR assumes any ringing must be a new call.

4.9.5 The response string may be either "typed" (that is, inserted into the
      keyboard buffer as if a user at the host PC had just typed it in), or it
      can be sent direct to the modem. The advantage of "typing" is that you
      can run a batch file to check times and do all sorts of other things. The
      advantage of sending direct to the modem is that the entire operation can
      take place in the background while an application continues running.

4.9.6 You may specify a response of up to 39 characters. If you expect the host
      PC to be at the DOS prompt when a call comes in, then it is a good idea
      to start with an escape key, so that DOS discards anything already typed
      and treats what follows as a new command.

      If all this sounds too complicated, but you still think you want to
      enable ring response, then have a look at the configuration scenario
      called "Home/Office via Modem" in section A5.

4.10  Reboot on loss of carrier

      Selecting this option will determine whether or not the computer will
      reboot when the modem reports that the carrier has been lost (presumably
      because the other end hung up). See scenario A5 for an example of an
      application taking advantage of this feature.

      The PC will not reboot unless there has been a TeleReplica session active
      since TRHOST was loaded.

4.11  Synchronize "baud" rate

      Selecting this option will determine whether or not TRHOST will attempt
      to match the "baud" rate being used by TR at the other end. This is
      useful if several users will all dial into the same host, but some users
      have slower modems than others. See scenario A2 for an example of this.

4.12  Send wakeup every 2 minutes

      Selecting this option will determine whether or not TRHOST will send a
      NULL character whenever two minutes has passed with no other activity. A
      single NULL is ignored by TR, but may serve to keep a connection to a
      mini-computer link. See scenario A4 for an example of this.

4.13  Private mode

      In private mode, the screen of the host PC will be blank, and the
      keyboard of the host PC will be inactive (including CTRL-ALT-DEL). This
      is useful to enhance privacy when the host PC is in a public location.
      Note that the screen blanking has only been tested on VGA, EGA, CGA and
      Hercules display cards, and only in text modes. It has worked correctly
      with all the applications tested, but you should test it with your own
      applications and display cards before relying on it!

4.14  Printer redirection

      When a TeleReplica session is active, it is possible to redirect printer
      output (which would otherwise be printed at the host PC) so that it is
      printed at the replica PC instead. When no session is active, the host
      will print normally even though TRHOST is still loaded.

4.15  Create consistent .TR file

      Once TRHOST has been installed correctly, TRHOSTIN can create a
      configuration file for TR that is consistent (same "baud" rate, password,
      use of carrier detect etc). It will normally still be necessary to edit
      this file to do some fine tuning, but the work required will be less than
      if you started with the vanilla TR.TR file distributed with TR.

4.16  Abandon Changes

      If you have made a mistake, or if you only wanted to see what the current
      settings were, then this option allows you to quit without making any
      changes.

4.17  Save Changes and Leave Installation Program

      This is the normal way to exit this program when you have made all the
      required changes. The relevant files (TRHOST.EXE, TRGET.EXE, TRPUT.EXE
      TRTALK.EXE, TRDIAL.EXE, TREXTR.EXE, TREXTS.EXE and TRMODSET.EXE) will all
      be modified appropriately.

      Note that the executable files are actually modified, so beware of virus
      protection programs which compute checksums for executable files - they
      are likely to report possible virus infections after installation! The
      alternative (loading configuration information from a disk file) was
      rejected due to the additional memory required for the file processing
      code...


5.    Replica Installation

      To install TeleReplica at the replica computer, first copy the files:
      TR.EXE, TR.HLP, and TR.TR (or better still the .TR file that was created
      during host installation) into a directory (say \TR). Then use a text
      editor to edit the .TR file. This file should look something like:

      ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
          TeleReplica Configuration File
          Do NOT change the order of these parameters, or delete any lines!

      "COM1"                Communications port ("COMn" or base/interrupt)
      2400                  "Baud" rate (typically 300, 1200, 2400, or 9600)
      "COMSPEC"             Pathname for DOS Command Interpreter (or "COMSPEC")
      07                    Attribute for normal text (such as help screen)
      47/70                 Attribute for file transfer monitoring
      4F/0F                 Attribute for pop-up windows
      "trput %s\r"          Host command to send (download) files
      "trget\r"             Host command to receive (upload) files
      0                     Printer (normally 0, 1 or 2)
      440                   Frequency of "bell" tone (Hz)
      100                   Duration of "bell" tone (ms)
      256                   Block size for file upload (1-256)
      8                     Number of block buffers for upload (1-8)
      111                   Length of "break" (ms)
      3000                  Time to wait for first char before timeout (ms)
      500                   Time to wait for subsequent chars in block (ms)
      56                    Time to wait between "typing" keys (ms)
      "password"            Password to log in to host computer
      "MODEM"               Type of link (MODEM, DIRECT, or OTHER)
      "NONE"                Flow control (CTS, XON, BOTH or NONE)
      "YES"                 Send BREAKs to host computer
      "YES"                 Use BIOS for keyboard input
      "[TR] %s"             DOS shell prompt format string
      "LRCA"                Local command shifts (Left, Right, Ctrl, Alt)
      ""                    Connect command for modem
      ""                    Disconnect command for modem

          Each of the remaining lines must contain 3 strings and a number.
          The first string is the trigger string to search for.
          The second string is the response to be sent after the trigger.
          The third string is the response to be sent after timeout.
          The number is the time to wait before timeout (in ms).
      ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

      Most of these parameters will not need to be changed.

5.1   The serial port may be one of the standard ones ("COM1", "COM2", "COM3",
      or "COM4") or you may specify the base address and interrupt number [e.g.
      COM1 would be 03F8/IRQ4]. For compatibility with previous versions of TR,
      you may also use a hex interrupt vector number, so that a third way to
      specify COM1 is 03F8/0C.

5.2   The "baud" rate should be set appropriately for the modem.

5.3   The DOS command interpreter should normally be taken from the COMSPEC
      environment variable. However, if this does not work (or does not select
      the desired command interpreter) the full path name of a command
      interpreter can be specified (e.g. "C:/DOS/COMMAND.COM" - or
      "C:\\DOS\\COMMAND.COM" - the \\ is needed since \ introduces an escape
      sequence).

5.4   Video attributes are two hexadecimal digits: the first is the background
      color, and the second is the foreground color. Optionally a second
      attribute may be specified (e.g. 4F/70) - the first attribute is used for
      color displays and the second is used for monochrome systems (this allows
      a single control file to work without change with different displays).

5.5   When the user running TR requests a file transfer, TR "types" the
      necessary command at the host PC. These two lines should not be changed
      except possibly to fill in a full path name if TRGET.EXE and TRPUT.EXE
      are not in the path of the host PC.

5.6   When host printing is being redirected to the replica computer's printer,
      TR needs to know which printer to use. LPT1: is printer 0, LPT2: is
      printer 1, and LPT3: is printer 2. Serial printers are not directly
      supported.

      Note that it is not necessary or possible to specify which host printer
      is to be redirected; anything sent to LPT1:, LPT2: or LPT3: will be
      redirected. This was done to save the user the trouble of working out
      which printer the host was using.

5.7   The frequency (or pitch) and the duration of the "bell" can be modified
      to suit your personal preferences (and the volume of your PC's speaker!).
      The "bell" is used to indicate that some corruption of the data being
      received by TR has occurred.

5.8   The size of file transfer blocks and the number of buffers should not
      need to be changed, except on a very poor 'phone line (in which case
      smaller blocks and fewer buffers may improve matters). However, if the
      line is this bad then TR will probably be unusable anyway...

5.9   The length of "break" required is not likely to need to be changed -
      unless perhaps a mini-computer requires longer?

5.10  During a file transfer, TR will wait a certain time for the start of each
      block. If nothing has been received within the time, then TR will request
      the block be sent again (since presumably it got lost).

5.11  Once the first character in a block has been received, the rest should
      follow immediately - any gap probably means problems. However, when using
      an overloaded mini-computer link (or using a packet network that may
      introduce delays between packets, or using a modem with error correction,
      compression or bps translation) this parameter could need to be longer.

5.12  Since on many PCs (especially ones with CGA displays) interrupts are
      disabled for LONG periods when writing to the screen, it is usually
      necessary to make TR pretend to type quite slowly, especially when
      sending things like file transfer commands. If you find you are losing
      characters under these circumstances, then make this delay longer; if you
      have a smart BIOS and/or version of DOS and/or command interpreter then
      you may be able to get away with a shorter delay (even 0 ms). On all the
      systems I have used, the time taken to send two characters at 2400 bps or
      below is sufficient, so this delay is probably only needed above 2400
      bps.

5.13  The password must match the password installed in TRHOST at the host
      computer.

5.14  There are three kinds of link that may be used between two PCs:
      MODEM    Use this if you are working with a modem that provides CARRIER
               DETECT (note that you will require an appropriate cable [see
               Appendix C1] and possibly some initialization of the modem [see
               the start of Appendix A]).
               You can also use this if you are using a null modem cable that
               provides a CD line (see Appendix C3).
      DIRECT   Use this if you are working with a three-wire null modem cable,
               or if you are using a modem/cable that cannot provide accurate
               CD information.
      OTHER    Use this if you are working with a mini-computer link (see
               scenario A4), or for initial modem setup (see the start of
               Appendix A).

5.15  TR can use the following flow control systems:
      NONE     No flow control. Use this with a direct cable or with modems
               that require no speed adjustment.
      CTS      Hardware flow control using RTS (request to send) and CTS (clear
               to send). Use this in preference to software flow control if it
               is available.
      XON      Software flow control using XON and XOFF (^S/^Q). Use this if
               flow control is needed and hardware flow control is not
               available.
      BOTH     Use both software and hardware flow control.

      See the discussion of flow control under host installation for further
      details.

5.16  Normally TR should send BREAKs to TRHOST, but see scenario A4 for use
      with a mini-computer link.

5.17  Normally TR will use the BIOS for keyboard input. However, many BIOSes
      filter out keys from enhanced keyboards (e.g. <F11>), and if use of these
      keys is important then it may be necessary to NOT use the BIOS, but
      rather to use the keyboard input buffer directly. Note however that some
      keyboard enhancing programs (such as Newkey) will only work with the BIOS
      setting. This is because they intercept the keyboard interrupt and store
      keys away in some place other than the standard buffer area, so that TR
      cannot find them!

5.18  The DOS prompt for when you are in a TR shell can be edited to suit your
      individual preferences - the %s inserts the original prompt.

5.19  If you don't like the default <Ctrl-Alt-LeftShift-RightShift> key
      combination to access local commands in TR, then you can change this to
      any other combination of these four main shift keys ("CAL" would mean
      <Ctrl-Alt-LeftShift> for example) - see scenario A3 for an application of
      this).

5.20  The connect command for the modem is sent when TR starts running (this
      will often be a dial command). The modem command strings here have the
      same format as those described above for the host computer installation
      (with the addition of a \B escape sequence that causes TR to transmit a
      BREAK). Make sure you leave the double quotes (") around each string!

5.21  The disconnect command is sent when TR terminates (using exit option 3
      only).

5.22  The automatic response strings at the end of the file can be used to
      respond to modem status messages. For example, if the replica computer's
      modem is not set to auto-answer, then TR may need to respond to a "RING"
      message from the modem by answering the 'phone - see scenario A5 for an
      application. These strings can also be used to achieve an automatic login
      to a mini-computer - see scenario A4 for an example. The trigger strings
      are only active before a TR-TRHOST link is established. They are also
      disabled once the final trigger string has been detected.

      Please note that since this file contains the password, anyone who
      obtains a copy of this file can potentially access the host computer!


6.    How to Use TeleReplica

      The following instructions assume that TeleReplica has been correctly
      installed (see sections 4 and 5). Only general guidelines are given here;
      more details are provided in the scenarios in Appendix A.

6.1   Host Computer

      First run the TRHOST program. If the replica computer is to originate the
      'phone call, then this may be all that is necessary.

      If the host computer is to originate the call, then use the command:
            TRDIAL
      or
            TRDIAL number
      depending on how the dialing format string was installed.

      Once TRHOST is resident and the call is established, the host computer
      can be used normally. The only difference is that everything that appears
      on the screen is also being replicated on the replica computer's screen.

      The best way to remove TRHOST from memory is to run TRREMOVE. It is also
      possible to use utilities such as marknet/relnet. Note that some common
      mark/release utilities can NOT be used, because they do not restore the
      interrupt mask register.

6.2   Replica Computer

      Use the command:
            TR                     [use TR.TR configuration file]
      or
            TR filename            [use filename.TR configuration file]

      If the replica computer was to originate the call, then the modem
      initialization string in the configuration file will usually include a
      dial command to call the host computer.

      If the host computer was to originate the call, then the initialization
      string may contain an answer 'phone command. Note that in this case it is
      important that the TR program not be run until after the 'phone starts
      ringing! (Alternatively, there may be no initialization string, but
      instead there may be a trigger string to respond to RING from the modem -
      see scenario A5.)

      If the configuration file contains no modem initialization string, then
      the user at the remote computer can enter modem commands manually. This
      may be convenient for a consultant wishing to dial many different
      clients. (Before a carrier is detected, TR will behave much like a normal
      communications program.)

      Once both TR and TRHOST are running and connected to each other, they
      will automatically adjust the host computer's "baud" rate (if this
      feature is enabled) and the host computer will check the password
      provided by the replica computer. Provided the password is correct, the
      replica computer will effectively be able to take over the host computer,
      or alternatively to observe whatever the host computer is doing. Any key
      typed on the replica computer will be acted upon by the host computer,
      and anything that appears on the host computer's screen will also appear
      on the replica computer's screen.

      It is sometimes necessary to execute a command on the replica computer,
      rather than transmitting the keystroke to the host computer. This is
      achieved by holding down some combination of left shift, right shift,
      ctrl and alt all at the same time (the exact combination is specified in
      the .TR file currently in use). When you do this a list of all the
      possible commands will be displayed, and you can then type the required
      command key:

      F2      simulate a carrier signal (useful if the modem does not provide
              this information) [link type should be OTHER to use this command]
      Ctrl-F2 simulate NO carrier signal (opposite of F2)
      F6      send break, restart session [use this if TeleReplica locks up -
              very rare!]
      F8      reboot the host computer (useful if host computer "hangs" for any
              reason, but make sure TRHOST is run from AUTOEXEC.BAT!)
      F9      shell directly to DOS, return to TR later by typing "exit"
      F10     exit TeleReplica [optionally shell out and return later]
      Home    refresh display from HOST [use this if a bad 'phone line messes
              up the screen]
      PgUp    upload file using DMP protocol [transfer file(s) from replica to
              host]
      PgDn    download file using DMP protocol [transfer file(s) from host to
              replica]

      Note that before performing a file transfer, the host computer must be at
      the DOS prompt, and TRGET.EXE and TRPUT.EXE must be accessible in the
      current path (or alternatively the .TR file must contain full paths, not
      just (say) TRGET but rather C:/TR/TRGET - note forward slashes!). If
      TRGET/TRPUT cannot be found, then the host will display a "command not
      found" error message, but TR will go on waiting for a response from
      TRGET/TRPUT! Pressing any key will terminate this waiting and bring up an
      appropriate error message.

      If a file transfer needs to access a file in another directory, it may be
      convenient to shell out of TR, change directories, and then exit from DOS
      back into TR to start the file transfer. TR will transmit any path that
      you specify, so if the two PC's have equivalent directory structures it
      is easy to transfer files to the corresponding directory on the other PC
      (see Appendix B for a sample file transfer session).


7.    TeleReplica Utility Programs

7.1   TRREMOVE

      This will search for a copy of TRHOST loaded in memory. If one is found,
      then it is checked to see whether it is currently in use (if so, TRREMOVE
      will ask for confirmation before removing it). If it is not in use, or if
      it is to be removed anyway, all interrupts, the interrupt mask register
      and the serial chip state are restored to their initial state when TRHOST
      started running, and TRHOST's memory is freed.

      Please note that as with most TSR programs, this may not work unless
      TRHOST was the most recent TSR to be loaded. In general TSR programs
      should be unloaded in the reverse order they were loaded. In this case
      "not working" means that any TSR loaded after TRHOST may cease to
      function. If this is not possible then the use of marknet/relnet (or some
      other mark/release utility that preserves the interrupt mask register as
      well as the vectors) is recommended.

      It is sometimes convenient to be able to keep a modem connection even
      though TRHOST is being unloaded. Normally, TRREMOVE will restore the
      serial port state to its original state when TRHOST was first run.
      However, it is possible to force the DTR line to be left active by
      entering:
            TRREMOVE ON
      and DTR can be forced off by entering:
            TRREMOVE OFF
      If either ON or OFF is specified, then TRREMOVE assumes you know what you
      are doing and does not ask for confirmation even if a link is active,
      allowing TRREMOVE to be used in a batch file on the host PC without
      pausing for input.


7.2   TRHOSTC

      This program works much like TRHOSTIN, except that instead of modifying
      files on disk it modifies the copy of TRHOST currently active in memory.
      Not all parameters may be altered "on the fly" - for example, the COM
      port cannot be altered mid-session. The anticipated use for this program
      is to do things like turning private mode on or off for just part of a
      session...

      Note that the copy of TRHOST.EXE on disk is not modified.


7.3   TRTALK

      TRTALK will allow the users at the host and replica computers to "talk"
      to each other. Anything that is typed at the host computer is displayed
      in the top half of the screen, and anything that is typed at the replica
      computer is displayed in the bottom half of the screen.

      TRTALK sends a special command to TR to tell TR that talk mode is
      required, so that TR will send keys in a way that can be distinguished
      from the host keys. If this command is lost, then what is typed at either
      end will appear in the top window! If this happens, simply exit TRTALK
      (Alt-X) and run it again.

      TRTALK also sends a special command to TR to tell TR to end talk mode. If
      this command is lost, then TR will behave normally unless a program that
      uses shift-key status is run, which will cause problems because in talk
      mode TR does not send shift status information! To correct this problem,
      use local TR command <F2> (simulate carrier), since a side effect of this
      command is to end talk mode.


7.4   TREXTS and TREXTR

      These programs are normally called from TRSZ.BAT and TRRZ.BAT
      respectively. They allow a clean interface between TeleReplica and
      external file transfer programs such as DSZ.

      These programs are an exception to the rule that TRHOSTIN installs only
      programs used at the host end; TREXTS.EXE and TREXTR.EXE both need to run
      at both ends, so they must be installed for the correct modem port etc on
      the replica as well as the host.

      Once TRHOSTIN has installed these programs correctly on both the host and
      the replica, and TRRZ.BAT, TRSZ.BAT and the external protocol program
      (such as DSZ.EXE) are in some directory on the path of both the host and
      replica, file transfer is quite simple:

7.4.1 To download a file from the host PC to the replica PC, simply enter the
      following command on the host PC:
            trsz <filename> ...
      and TR will automatically run TRRZ on the replica without you doing
      anything!

7.4.2 To upload a file from the replica PC to the host PC, first ensure that
      the host PC is at the DOS command prompt. Then shell out of TR (using
      local F9). Finally enter the following command on the replica PC:
            trsz <filename> ...
      and TRHOST will automatically run TRRZ on the host.

      TRRZ.BAT, TRSZ.BAT, TREXTS.EXE and TREXTR.EXE all pass parameters on to
      the external protocol program, so parameters other than file names can be
      used if desired.

      TREXTS.EXE and TREXTR.EXE recognize one special parameter:
            #portx#
      which will substitute in the DSZ portx <base>,<IRQ> command. This allows
      TRRZ.BAT and TRSZ.BAT to remain unchanged even when TeleReplica is
      installed for a different port. See the supplied TRRZ.BAT and TRSZ.BAT
      for examples of this.


7.5   TRMODSET

      Usage: TRMODSET [-fr] [filename]

      TRMODSET will send all the commands in TRMODSET.DAT (or in filename.DAT
      if specified) to the modem, waiting for an "OK" response to each command.
      This is useful to set up very complicated parameters necessary for some
      of the more sophisticated modems. It assumes a modem that uses the Hayes
      AT command set (at least at&f to restore factory defaults and OK in reply
      to a good command).

      The -r command line option will cause TRMODSET to start with an "at&f"
      command to reset the modem to factory defaults, just in case a previous
      program has left the modem in a peculiar state. The "at&f" is sent before
      TRMODSET starts monitoring for command echo or "OK" responses.

      If a carrier is present when TRMODSET runs then it will exit without
      doing anything unless the "-f" (for "force") command line argument is
      present. This allows TRMODSET to be run from AUTOEXEC.BAT without
      disrupting an existing connection if the host PC needs to be rebooted.

      Note that TRMODSET is installed by TRHOSTIN, so if you want to use
      TRMODSET on the replica PC you will need to install the host programs on
      the replica PC (once installed, the other host programs may be deleted,
      but they must be present for TRHOSTIN to run).

      Note also that you cannot use TRMODSET to set the modem to "no echo" or
      "quiet" modes, since TRMODSET monitors that commands are being echoed and
      that the modem is responding with "OK" to each command.


7.6   TRCHECK

      TRCHECK checks to see if the current time is within a specified range,
      and returns the DOS errorlevel set to 0 if within the range and 1 if
      outside the range. The following code might appear in an AUTOEXEC.BAT
      file on a host computer:
            trcheck 9:00:00 17:00:00
            if not errorlevel 1 goto done
            trhost
            :done
      The effect of this is to first check to see if the time is between 9AM
      and 5PM. If so, then errorlevel is set to 0, and nothing further happens.
      However, if the time is not between 9 and 5, then trhost will be run.

      This has proved valuable when TRHOST must run on an office computer
      outside normal working hours, but the computer must be used normally
      during the day. See also scenario A5 for a further application.


7.7   TRASK

      Usage: TRASK <timeout> <prompt> <answers>

      TRASK works much like a normal batch file enhancing ASK program, except
      that it has a timeout. This is useful when a computer will usually be
      used as a TeleReplica host, but sometimes must be used locally. Rather
      than having to boot from a different disk, the following code might
      appear in an AUTOEXEC.BAT file on a host computer:
            @echo off
            path c:\tr
            trask 5 "Do you want to load TRHOST? (y/n)\a\a: " "yn"
            if errorlevel 1 goto no
            trhost
            :no
      The effect of this is to run TRHOST if the user presses the 'y' key or if
      no key has been pressed after 5 seconds. If a user is at the computer and
      answers 'n' then TRHOST will not be loaded. See scenario A5 for an
      example of this.

      TRASK returns an errorlevel that depends on the <answers> string: the
      first letter in this string (or a timeout) returns error level 0, the
      second returns error level 1 and so on. Case is not significant unless
      the <answers> string contains the same letter in both upper and lower
      case.

      TRASK is a public domain program and may be distributed separately.


      APPENDIX A - Configuration Scenarios

      The following are specific situations in which TeleReplica has been used.
      The descriptions of the situations, and the resulting configurations of
      TeleReplica, are presented in detail. It is hoped that seeing the way
      TeleReplica was installed in some typical applications will help when it
      comes to installing TR for your own situation.

      Note that unless otherwise stated, all modems are assumed initially to be
      in the TeleReplica default state, to be connected to the PC via a 25-way
      straight-through modem cable, and to be Hayes-AT-command-compatible. To
      get a Hayes-AT-command-compatible modem into the TeleReplica default
      state the following commands should be sent to the modem using any normal
      communications program (or using TR SETUP or using TRMODSET):
            at &f         restore modem to "factory default"
            at &c1        modem should report true carrier status
            at &d2        modem should take notice of DTR to hang up 'phone
            at x4         (optional) give detailed status messages etc
            at &w         save current state for future use (the state is saved
                          in non-volatile RAM, so that this setup only needs to
                          be done once unless some other program interferes)


A1.   Consultant/Client via Modem

A1.1  Here the consultant is running a 2400 bps modem connected to COM1, and
      the client (whom we will call Fred) is running a similar modem also
      connected to COM1. Both computers are equipped with EGA color display
      cards. The consultant will be performing the TRHOST installation for the
      client, and then sending the client the installed version ready to run.

      When the client wants help, he will call the consultant (a normal voice
      call). When both parties are ready TeleReplica must take over the call.

A1.2  First the consultant must run TRHOSTIN, and make the changes necessary to
      achieve the following display:
      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º TeleReplica Host 3.20 Installation Copyright (c) 1992 Douglas Thomson º
      º                                                                       º
      º    A. Select serial port (currently COM1)                             º
      º    B. Change password (currently "Fred's password")                   º
      º    C. Change modem initialization string (currently:                  º
      º       "")                                                             º
      º    D. Change modem dialing format string (currently:                  º
      º       "ata\r")                                                        º
      º    E. Select maximum "baud" rate (currently 2400)                     º
      º    F. Use modem CARRIER DETECT signal (currently YES)                 º
      º    G. Flow control (currently NONE)                                   º
      º    H. Generate INT 9 on each key (currently NO)                       º
      º    I. Respond to modem RING signal (currently NO)                     º
      º    J. Reboot on loss of carrier (currently NO)                        º
      º    K. Synchronize "baud" rate (currently YES)                         º
      º    L. Send wakeup every 2 minutes (currently NO)                      º
      º    M. Private mode (currently NO)                                     º
      º    N. Printer redirection (currently HOST)                            º
      º    O. Create consistent .TR file                                      º
      º    Q. Abandon changes                                                 º
      º    S. Save changes and leave installation program                     º
      º                                                                       º
      º Selection:                                                            º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
      Refer to section 4 for the meaning of each option. Since both modems run
      at the same speed it does not matter whether "baud" rates get
      synchronized or not. Since Fred will only run TRHOST when he wishes to
      get help from the consultant, the password is not important. The modem
      dialing format string simply answers the 'phone - or more accurately,
      since the 'phone will already be in use for the voice call, it causes the
      modem to take over the call in "answer" mode.

      Next the consultant selects option O from the main menu, and enters the
      name of the configuration file he wishes to use for Fred:
      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º TeleReplica Host Program .TR File Name Selection                      º
      º                                                                       º
      º Edit existing string:                                                 º
      º fred                                                                  º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      Finally the consultant exits TRHOSTIN by selecting option S to save the
      changes. The consultant can now send Fred a disk with all the installed
      TeleReplica files on it (note that the consultant should also send Fred
      an unaltered original copy of the TeleReplica files in case Fred wants to
      pass them on to anyone - see the LICENCE.DOC file for details).

A1.3  Now the consultant needs to edit the file named FRED.TR to make a few
      alterations (TRHOSTIN only provides a starting point...). In particular,
      the following line must be changed:
            ""                Connect command for modem
      to:
            "at d\r"          Connect command for modem
      This command tells the modem to go "off hook" and take over the call in
      "originate" mode.

      This completes the installation stage.

A1.4  When Fred wants some help, he will run TRHOST and then 'phone the
      consultant and explain the problem. When the consultant is ready, he will
      enter the command:
            TR FRED
      and then instruct Fred to enter the command:
            TRDIAL
      and hang up the 'phone as soon as he (Fred) hears his modem making a
      "screaming" noise. After giving these instructions (and thus while Fred
      is still typing) the consultant will hang up his 'phone. Fred will finish
      entering the TRDIAL command, and hang up when he hears the screaming
      noise. TeleReplica will then take over the call, synchronize "baud"
      rates, exchange passwords, and give the consultant control of Fred's
      computer.

A1.5  When the consultant is finished, he will exit TR using option 3, which
      will cause the modem to hang up and terminate the 'phone call.

      Fred can either leave TRHOST running (it will do no harm, and uses less
      than 10K of memory), or else use TRREMOVE to uninstall TRHOST.


A2.   Remote/Shared via Modem

A2.1  Here a remote user wishes to connect into a local area network, and one
      node in the LAN is dedicated to this purpose. The main problem is that
      since the LAN node will be unattended, all it takes is one user to run a
      program which "hangs" the computer, and then no-one will be able to dial
      in until someone pushes the reset button on the node PC! However, in this
      scenario there is a modem-controlled switch box which turns on power to
      the node PC as soon as the 'phone starts ringing, and leaves the power on
      until either a minute or so has elapsed with no carrier being
      established, or until the carrier is lost (which will happen when the
      remote user hangs up). [These switch boxes are (I believe) commercially
      available, and indeed the electronics required is trivial to someone who
      feels at home with circuit diagrams and a soldering iron. We have several
      home-made ones in use here at MUCG.] This means there is no problem if a
      user "hangs" the computer; just hang up and then dial in again, and the
      computer will have been powered down and come up again clean!

      The node PC has a 2400 bps modem connected to COM2, and the remote user
      is running a 1200 bps modem connected to COM1. The node PC is equipped
      with a CGA color display card (with no monitor required). The remote PC
      is equipped with a Hercules monochrome display.

      The LAN manager will be performing the TRHOST installation for the node
      PC, and then providing all the remote users with a disk that is almost
      ready to go.

      The 'phone number of the node PC is 123 4567.

A2.2  First the LAN manager must run TRHOSTIN, and make the changes necessary
      to achieve something like the following display:
      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º TeleReplica Host 3.20 Installation Copyright (c) 1992 Douglas Thomson º
      º                                                                       º
      º    A. Select serial port (currently COM2)                             º
      º    B. Change password (currently "sdggsdjgxvwept97867km,.mvikjdsdh")  º
      º    C. Change modem initialization string (currently:                  º
      º       "\rata\r")                                                      º
      º    D. Change modem dialing format string (currently:                  º
      º       "\r%s\r")                                                       º
      º    E. Select maximum "baud" rate (currently 2400)                     º
      º    F. Use modem CARRIER DETECT signal (currently YES)                 º
      º    G. Flow control (currently NONE)                                   º
      º    H. Generate INT 9 on each key (currently NO)                       º
      º    I. Respond to modem RING signal (currently NO)                     º
      º    J. Reboot on loss of carrier (currently NO)                        º
      º    K. Synchronize "baud" rate (currently YES)                         º
      º    L. Send wakeup every 2 minutes (currently NO)                      º
      º    M. Private mode (currently NO)                                     º
      º    N. Printer redirection (currently HOST)                            º
      º    O. Create consistent .TR file                                      º
      º    Q. Abandon changes                                                 º
      º    S. Save changes and leave installation program                     º
      º                                                                       º
      º Selection:                                                            º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
      Refer to section 4 for the meaning of each option. Note that the modem
      initialization string answers the 'phone - this is nice in the case of
      timed call charges, since the remote user does not pay for the time it
      takes the PC to boot. Since some remote users will dial in at 2400 bps,
      TRHOST must be installed for 2400; but since other remote users will dial
      in at 1200 bps it is essential that "baud" rates get synchronized. Since
      anyone could try to get into the LAN via the node PC the password is very
      important - notice that it is both long and quite random.

      Next the LAN manager selects option O from the main menu, and enters the
      name of the configuration file he wishes to use for the node PC:
      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º TeleReplica Host Program .TR File Name Selection                      º
      º                                                                       º
      º Edit existing string:                                                 º
      º lan1                                                                  º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      Finally the LAN manager exits TRHOSTIN by selecting option S to save the
      changes. He can now make up a disk with all the installed TeleReplica
      files on it to give to the remote users, but first he must edit the
      LAN1.TR file to install the node PC's 'phone number. This means changing
      the line:
            ""                Connect command for modem
      to:
            "at d 123 4567\r" Connect command for modem
      so that when remote users run TR the number will be dialed automatically.
      Also, since modems more often use COM1 than COM2, the LAN manager should
      probably edit the line:
            "COM2"            Communications port (COMn or base/interrupt)
      to become:
            "COM1"            Communications port (COMn or base/interrupt)

A2.3  Now the remote user needs to edit his personal copy of the file named
      LAN1.TR to work at 1200 bps. The line containing:
            2400              "Baud" rate (typically 300, 1200, 2400, or 9600)
      must be changed to:
            1200              "Baud" rate (typically 300, 1200, 2400, or 9600)

      This completes the installation stage.

A2.4  When the remote user wishes to connect into the LAN, he will enter the
      command:
            TR LAN1
      This will cause the modem to dial the node PC, which will cause the modem
      switch box to turn on the power to the node PC, which will boot and then
      run TRHOST, which will make the node PC's modem answer the call.
      TeleReplica will then synchronize "baud" rates, exchange passwords, and
      give the remote user control of the node PC.

A2.5  When the remote user is finished, he will exit TR using option 3, which
      will cause the modem to hang up and terminate the 'phone call. The node
      PC will then be powered down until the next call.


A3.   Laptop/Desktop via Direct Cable

A3.1  Here someone wishes to connect a laptop computer to a desktop computer
      via a three-wire null modem cable. The reason for this is that the
      desktop only has a 5.25" disk, and the laptop only has a 3.5" disk, and
      it is necessary to transfer files between the two systems. The desktop
      computer is a 20MHz 80386, and the laptop is a 12MHz 80286. The cable is
      connected from COM1 on the desktop to COM1 on the laptop. The desktop has
      a VGA color display; the laptop has a gas plasma display that emulates
      EGA.

      It does not matter which PC is the host, but for the sake of this example
      we will assume the desk PC will be the host.

      The laptop computer has its <Del> key right next to <RightShift>, so the
      user does not wish to be using <Ctrl-Alt-LeftShift-RightShift> for fear
      of accidentally rebooting the computer. <Ctrl-Alt-LeftShift> seems a
      safer combination.

A3.2  First the user must run TRHOSTIN, and make the changes necessary to
      achieve something like the following display:
      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º TeleReplica Host 3.20 Installation Copyright (c) 1992 Douglas Thomson º
      º                                                                       º
      º    A. Select serial port (currently COM1)                             º
      º    B. Change password (currently "password")                          º
      º    C. Change modem initialization string (currently:                  º
      º       "")                                                             º
      º    D. Change modem dialing format string (currently:                  º
      º       "")                                                             º
      º    E. Select maximum "baud" rate (currently 38400)                    º
      º    F. Use modem CARRIER DETECT signal (currently NO)                  º
      º    G. Flow control (currently NONE)                                   º
      º    H. Generate INT 9 on each key (currently NO)                       º
      º    I. Respond to modem RING signal (currently NO)                     º
      º    J. Reboot on loss of carrier (currently NO)                        º
      º    K. Synchronize "baud" rate (currently NO)                          º
      º    L. Send wakeup every 2 minutes (currently NO)                      º
      º    M. Private mode (currently NO)                                     º
      º    N. Printer redirection (currently HOST)                            º
      º    O. Create consistent .TR file                                      º
      º    Q. Abandon changes                                                 º
      º    S. Save changes and leave installation program                     º
      º                                                                       º
      º Selection:                                                            º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
      Refer to section 4 for the meaning of each option. Notice that the "baud"
      rate is set to 38400 for fast file transfers (this works well on my test
      system, but slower speeds may be needed on other systems - experiment!).
      Obviously here the password is not important. Since the three-wire cable
      will not provide any carrier information, it is essential that carrier be
      ignored.

      Next the user selects option O from the main menu, and enters the name of
      the configuration file he wishes to use for the desktop:
      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º TeleReplica Host Program .TR File Name Selection                      º
      º                                                                       º
      º Edit existing string:                                                 º
      º desk                                                                  º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      Finally the user exits TRHOSTIN by selecting option S to save the
      changes.

A3.3  Next the user needs to edit the file named DESK.TR to use the shift key
      combination required for the laptop. The line containing:
            "LRCA"            Local command shifts (Left, Right, Ctrl, Alt)
      must be changed to:
            "LCA"             Local command shifts (Left, not Right, Ctrl, Alt)

      The user can now copy the installed files onto a 5.25" floppy disk, take
      the disk to a computer that has both 5.25" and 3.5" inch drives, and copy
      the file onto a 3.5" disk for the laptop.

      This completes the installation stage.

A3.4  When the user wishes to connect the two computers, he will enter the
      command:
            TRHOST
      on the desktop, and the command:
            TR DESK
      on the laptop. This will cause TeleReplica to synchronize "baud" rates,
      exchange passwords, and give the user control of the desktop computer
      from the laptop. Files can now be transferred at almost 3.8K per second!

A3.5  When the user is finished, he will exit TR using option 3, which will
      take the laptop back to normal, but leave TRHOST in the desktop's memory
      (see A1.5 for further discussion of this).


A4.   Remote/Shared via Common Mini-computer

A4.1  Here a remote user wishes to connect into a local area network, and one
      node in the LAN is dedicated to this purpose. There is no direct link
      between the PCs; instead, both the node PC and the remote user must log
      into the same mini-computer and run a link program (such as trfifo) to
      establish a connection via the mini-computer.

      One problem is that since the LAN node will be unattended, all it takes
      is one user to run a program which "hangs" the computer, and then no more
      remote users will be able to connect to the LAN until someone pushes the
      reset button on the node PC! (Note that TeleReplica does support
      rebooting the host PC, but this can only work if interrupts are not
      disabled and if the relevant code has not been overwritten. As a rule,
      TeleReplica can get out of any situation that <Ctrl-Alt-Del> could get
      out of, but if the hardware reset button was needed TR would be
      helpless.)

      Another potential problem is that if one user exits TR while still logged
      in to the LAN, then the next user could pick up the session! This is
      avoided by having the link program send a "reboot" command to the node PC
      when the link is broken.

      Trfifo cannot pass BREAKs from one end to the other; instead, BREAK is
      used to terminate the execution of trfifo. This means that TR must not
      send a BREAK unless it wants to kill the link.

      To make life complicated, the mini-computer will automatically disconnect
      any terminal that does no input or output for 5 minutes. However, the
      node PC must remain connected to the mini-computer all day waiting for
      remote users to connect in.

      The mini-computer links are set at 9600 bps, and cannot be changed. Both
      computers are connected to the mini-computer via COM1, and both computers
      are running color displays (however, the dedicated node PC requires no
      monitor).

      The LAN manager will be performing the TRHOST installation for the node
      PC, and then providing all the remote users with a disk that is almost
      ready to go.

A4.2  First the LAN manager must run TRHOSTIN, and make the changes necessary
      to achieve something like the following display:
      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º TeleReplica Host 3.20 Installation Copyright (c) 1992 Douglas Thomson º
      º                                                                       º
      º    A. Select serial port (currently COM1)                             º
      º    B. Change password (currently "sdfddffgjkiou774htgjhgsduh875sdh")  º
      º    C. Change modem initialization string (currently:                  º
      º       "")                                                             º
      º    D. Change modem dialing format string (currently:                  º
      º       "")                                                             º
      º    E. Select maximum "baud" rate (currently 9600)                     º
      º    F. Use modem CARRIER DETECT signal (currently NO)                  º
      º    G. Flow control (currently NONE)                                   º
      º    H. Generate INT 9 on each key (currently NO)                       º
      º    I. Respond to modem RING signal (currently NO)                     º
      º    J. Reboot on loss of carrier (currently NO)                        º
      º    K. Synchronize "baud" rate (currently NO)                          º
      º    L. Send wakeup every 2 minutes (currently YES)                     º
      º    M. Private mode (currently NO)                                     º
      º    N. Printer redirection (currently HOST)                            º
      º    O. Create consistent .TR file                                      º
      º    Q. Abandon changes                                                 º
      º    S. Save changes and leave installation program                     º
      º                                                                       º
      º Selection:                                                            º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
      Refer to section 4 for the meaning of each option. The password is not so
      critical here, since a user must be able to log into the mini-computer
      before getting through to the node PC. The mini-computer line will not
      provide any carrier information, so this must be ignored. "Baud" rates
      must NOT be synchronized, since a NULL character transmitted at 2400 bps
      would be received as a BREAK by the mini-computer at 9600 bps! To avoid
      the node PC getting logged out, TRHOST must send a NULL character to
      "wake up" the mini-computer every few minutes. This will be ignored by
      TR.

      Next the LAN manager selects option O from the main menu, and enters the
      name of the configuration file he wishes to use for the node PC:
      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º TeleReplica Host Program .TR File Name Selection                      º
      º                                                                       º
      º Edit existing string:                                                 º
      º lan2                                                                  º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      Finally the LAN manager exits TRHOSTIN by selecting option S to save the
      changes. He can now make up a disk with all the installed TeleReplica
      files on it to give to the remote users.

A4.3  Due to the way trfifo buffers input (or possibly some other peculiarity
      of our mini-computer?) the delay between sending keys needs to be 165 ms
      to avoid losing characters! Therefore, the line containing:
            56                Time to wait between "typing" keys (ms)
      must be changed to:
            165               Time to wait between "typing" keys (ms)

      Also, since we are using a mini-computer link, the line containing:
            "DIRECT"           Type of link (MODEM, DIRECT, or OTHER)
      must be changed to:
            "OTHER"            Type of link (MODEM, DIRECT, or OTHER)

      Finally, TR is capable of automating the mini-computer login process. If
      this is desired, then something like the following lines must be added at
      the end of the file:
            "DISCONNECTED"      "\D250\r"               "\r"             5000
            "Enter RESOURCE ? " "\D100G9000\r"          "\r"             5000
            "CONNECTED TO"      ""                      ""               5000
            "login: "           "\D100doug\r"           "\B\r"            500
            "Password:"         "\D100password\r"       "\r"            10000
            "Selection: "       "\D100d\r"              ""              40000
            "/users/doug>"      "\D100trfifo lan2\r"    ""              40000
            "and run TR"        "\D1000"                ""              40000
      The exact strings will depend on the mini-computer. This example (apart
      from the password) works for the author.

      This completes the installation stage.

A4.4  When the remote user wishes to connect into the LAN, he will run TR:
            TR LAN2
      which will automatically log into the mini-computer and run trfifo to
      connect to the node PC (in this case lan2).

      TeleReplica will then synchronize "baud" rates, exchange passwords, and
      give the remote user control of the node PC.

A4.5  When the remote user is finished, he will exit TR using option 3, which
      will send a BREAK to the mini-computer. This will terminate the trfifo
      program which the remote user was running. The trfifo program that the
      node PC was running will detect that this has happened, and send a
      TeleReplica reboot command to the node PC to ensure that the next user
      cannot pick up anything the previous user left running. The node PC's
      trfifo program will then prepare for the next remote user. The node PC
      will complete rebooting, and run TRHOST from AUTOEXEC.BAT ready for the
      next remote login.

      [All this sounds complicated, but we use this system daily here at MUCG
      for some staff who have mini-computer lines but are too far away for LAN
      connections.]


A5.   Home/Office via Modem

A5.1  Here a user wishes to dial in from home and take over the PC on his desk
      at work. The office PC has a 2400 bps modem connected to COM2, and the
      home PC has a 2400 bps modem connected to COM1. The office PC is equipped
      with an EGA color display, and the home PC is equipped with a Hercules
      monochrome display.

      One problem is that since the office PC will be unattended, all it takes
      is for the user to run a program which "hangs" the computer, and that
      will be the end of the office PC until the user goes back to work and
      presses the reset button! (Note that TeleReplica does support rebooting
      the host PC, but this can only work if interrupts are not disabled and if
      the relevant code has not been overwritten. As a rule, TeleReplica can
      get out of any situation that <Ctrl-Alt-Del> could get out of, but if the
      hardware reset button was needed TR would be helpless.)

      Since the user is putting in overtime working at night without getting
      paid for it, it seems reasonable that the office 'phone should at least
      pay for the call. However, how can the office computer know when to call
      the user at home? One possibility would be to set up a batch file to run
      TRDIAL at a predetermined time. However, it would be better if the user
      could choose any convenient time. TeleReplica can achieve this by
      monitoring the RING signal from the modem, and responding appropriately.
      The basic idea is that the user will dial the office number, and then
      hang up as soon as the 'phone starts ringing. TeleReplica will detect the
      'phone ringing, and respond by calling the user at home.

      Since the user does not want to be bothered by nuisance calls from the
      office computer, TeleReplica needs to be quite selective about the ring
      patterns it will respond to. Too short a ring may mean a telephone
      company routine line test. Too long a ring will mean a person trying to
      ring the office. Even if the ring is the correct length, the user may
      still wish to guarantee no interruptions between 11PM and 7AM!

      The 'phone number of the office PC is 123 4567.
      The 'phone number of the home PC is 765 4321.

A5.2  First the user must run TRHOSTIN, and make the changes necessary to
      achieve something like the following display:
      ³ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      ³plica Host 3.20 Installation Copyright (c) 1992 Douglas Thomson        º
      ³                                                                       º
      ³Select serial port (currently COM2)                                    º
      ³Change password (currently "fhkjeuyibn4593874sefeh8631wjds874dffd")    º
      ³Change modem initialization string (currently:                         º
      ³"")                                                                    º
      ³Change modem dialing format string (currently:                         º
      ³"\r%s\r")                                                              º
      ³Select maximum "baud" rate (currently 2400)                            º
      ³Use modem CARRIER DETECT signal (currently YES)                        º
      ³Flow control (currently NONE)                                          º
      ³Generate INT 9 on each key (currently NO)                              º
      ³Respond to modem RING signal (currently YES)ÄÄÄÂÄ 1. too short  220 ms º
      ³Reboot on loss of carrier (currently YES)      ÃÄ 2. too long  5000 ms º
      ³Synchronize "baud" rate (currently YES)        ÃÄ 3. delay    10000 ms º
      ³Send wakeup every 2 minutes (currently NO)     ÃÄ 4. reset    10000 ms º
      ³Private mode (currently NO)                    ÃÄ 5. "type" response   º
      ³Printer redirection (currently HOST)           ÀÄ 6. response Ä¿       º
      ³Create consistent .TR file                             "\0x1Btrauto\r" º
      ³Abandon changes                                                        º
      ³Save changes and leave installation program                            º
      ³                                                                       º
      ³ion:                                                                   º
      ³ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
      Refer to section 4 for the meaning of each option. Since anyone could try
      to get into the office PC the password is important - notice that it is
      both long and quite random. The modem dialing format string permits ANY
      modem command to be sent direct to the modem. It is essential that TRHOST
      takes notice of the CD signal, since the host computer will be
      automatically rebooted if the carrier is lost (see below). The host
      computer is to monitor the 'phone ringing and respond accordingly (again,
      see below). "Baud" rate synchronization is not important here.

      Next the user selects option O from the main menu, and enters the name of
      the configuration file he wishes to use for the office:
      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º TeleReplica Host Program .TR File Name Selection                      º
      º                                                                       º
      º Edit existing string:                                                 º
      º office                                                                º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      Finally the user exits TRHOSTIN by selecting option S to save the
      changes. He can now make up a disk with all the installed TeleReplica
      files on it to take home.

      However, still on the office PC the user needs to create a batch file
      called TRAUTO.BAT, containing something like:
            trcheck 7:00:00 23:00:00
            if errorlevel 1 goto done
            trdial atd7654321
            :done
      which will check that the time is between 7AM and 11PM, and if so dial
      the user's home number. Note that the "atd7654321" contains no spaces!

      The user must also ensure that AUTOEXEC.BAT has the directory containing
      all the TeleReplica files on the path, and that TRHOST is run whenever
      the system boots. However, when the user is at the office he will not
      want TRHOST loaded, so AUTOEXEC.BAT should contain something like:
            @echo off
            prompt $p$g
            path c:\tr
            trask 5 "Do you want to load TRHOST? (y/n): " "yn"
            if errorlevel 1 goto no
            trhost
            :no
      This will ask the user at the host PC whether or not to load TRHOST, and
      if the user does not say no within 5 seconds TRHOST will be loaded
      anyway. If the user is at the office, then typing 'n' will prevent TRHOST
      from loading.

A5.3  At home the user needs to edit the file named OFFICE.TR to install the
      office PC's 'phone number. This means changing the line:
            ""                Connect command for modem
      to:
            "at d 123 4567\r" Connect command for modem
      so that when the user runs TR the number will be dialed automatically.

      Next, since the home modem is on COM1 the line:
            "COM2"            Communications port (COMn or base/interrupt)
      must become:
            "COM1"            Communications port (COMn or base/interrupt)

      Finally, TR should respond to the modem ringing by answering the 'phone.
      This means adding an extra line at the end of the file containing:
            "RING"       "\D250ata\r"       ""       40000
      (Note the \D250 to wait a little bit for the modem to finish sending the
      carriage return and line feed after RING before sending the answer
      command. With some modems this may not be necessary; with others, a
      different delay may work better. If the answer command is ignored, then
      try a different delay.)

      This completes the installation stage.

A5.4  Before leaving the office, the user must remember to reboot the PC (thus
      loading TRHOST) and leave it turned on! However, it would be a good idea
      to switch the monitor off.

      When the user is ready to dial into the office PC from home, he will
      enter the command:
            TR OFFICE
      This will cause the modem to dial the office PC. The user must then
      listen to the modem and wait until he hears the 'phone ring once. As soon
      as he hears this, he must press any key (say the space bar) to terminate
      the call. TRHOST will start a timer going when the 'phone rings, and then
      wait 10 seconds, keeping track of the total time the 'phone has spent
      ringing. If, during the 10 seconds, the 'phone was ringing for more than
      0.2 seconds but less than .9 seconds, then TRHOST will pretend to "type"
      the keys:
            <Esc>trauto<enter>
      The <Esc> will ensure that anything currently on the command line is
      ignored, and the trauto will run the TRAUTO.BAT script. The batch file
      will check that the time of day is reasonable, and then call the user
      back. When the user's 'phone rings, the modem will send the message:
            RING
      to the home PC, and TR will trigger on this to respond to the modem with:
            ata
      which will answer the 'phone. TeleReplica will then synchronize "baud"
      rates, exchange passwords, and give the user control of the office PC.

A5.5  When the user is finished, he will exit TR using option 3, which will
      cause the modem to hang up and terminate the 'phone call. The office PC
      will then automatically reboot, ready for the user to call in again.

      [This is probably the most complicated set up of all, but it is the one
      the author has found most useful, and is in daily use by a number of
      staff at MUCG.]


      APPENDIX B - Sample File Transfer Session

B1    In this example, we will assume that a good link has been established as
      described in scenario A2. The user has logged into the LAN from home, and
      wishes to transfer all the C source files from the LAN directories:
            F:\USERDATA\FRED\TEST
            F:\USERDATA\FRED\UTILS
            F:\USERDATA\FRED\PROBLEM
      to the corresponding directories on his home PC:
            C:\PROGRAMS\TEST
            C:\PROGRAMS\UTILS
            C:\PROGRAMS\PROBLEM
      The current working directory on the LAN PC is F:\USERDATA\FRED. The
      current working directory on the home PC is C:\TR.

      First, the user needs to make C:\PROGRAMS the current working directory
      on his home PC. To do this, he must hold down Ctrl, Alt, LeftShift and
      RightShift all at the same time! This will bring up a screen similar to:
      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º TeleReplica Copyright (c) 1992 Douglas Thomson                        º
      º                                                                       º
      º  Key         Effect                                                   º
      º  ===         ======                                                   º
      º  <F2>      - simulate carrier - not used with MODEM link              º
      º  <Ctrl-F2> - simulate NO carrier - not used with MODEM link           º
      º  <F6>      - send break, restart session                              º
      º  <F8>      - perform warm boot on host                                º
      º  <F9>      - shell to DOS                                             º
      º  <F10>     - exit TeleReplica                                         º
      º  <Alt-X>   - exit TeleReplica                                         º
      º  <Home>    - refresh display from HOST                                º
      º  <PgUp>    - upload file using DMP protocol                           º
      º  <PgDn>    - download file using DMP protocol                         º
      º                                                                       º
      º  <ESC>     - do nothing                                               º
      º                                                          Press key:   º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
      Then he should press <F9> to shell to DOS, and enter the command:
            CD \PROGRAMS
      to make C:\PROGRAMS the current working directory. Then he can enter the
      command:
            EXIT
      to return to TR.

      Next he needs to start the download. To do this he must again hold down
      Ctrl, Alt, LeftShift and RightShift, and then press <PgDn>. Another box
      will appear:
      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º Name(s) of file(s) to be downloaded (use DOS wildcards):              º
      º WARNING: Files with the same names on this PC will be overwritten!    º
      º                                                                       º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
      and he must enter the relative paths and wildcards:
      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º Name(s) of file(s) to be downloaded (use DOS wildcards):              º
      º WARNING: Files with the same names on this PC will be overwritten!    º
      º TEST\*.C TEST\*.H UTILS\*.C UTILS\*.H PROBLEM\*.C PROBLEM\*.H         º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      If there were some problem (for example, if TRPUT.EXE were not on the
      path of the LAN PC), then the following could be displayed:
      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º TeleReplica Error:                                                    º
      º no ready marker from host                                             º
      º Type <ESC> to continue:                                               º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      However, normally the download will then commence, leaving the following
      display:
            ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
            º File Transfer in Progress...                º
            º                                             º
            º File:       test\xyz.c                      º
            º                                             º
            º Error:                                      º
            º                                             º
            º Efficiency: 96.6%                           º
            º                                             º
            º You may:                                    º
            º    1. Abort the file transfer               º
            º    2. Shell to DOS                          º
            º                                             º
            º Selection:                                  º
            ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
      The number of bytes remaining to be transferred is displayed in the top
      right corner of the screen. The most recent error will be reported in the
      appropriate line of the box, and the efficiency of the transfer (relative
      to a perfect 10 bits per byte) may help to relieve the boredom while
      waiting for the transfer to complete! The box also indicates which file
      is currently being transferred.

      At this stage, the user can either wait for the transfer to finish, or
      else select option 2 from the menu and shell to DOS. In this case, he can
      use his home PC for other jobs while the transfer takes place in the
      background. TR will continue to display the number of bytes remaining in
      the top right corner until the transfer is completed, at which time the
      number in the top right corner will become the string "Completed" (or,
      possibly, "Doubtful" if one or more files could not be created on the
      home PC). However, the user must be careful not to do things like delete
      the file that is being downloaded!

      While shelled out to DOS in this way, the user may exit back into TR at
      any time. If the file transfer is still in progress, then the file
      transfer window will still be there; otherwise, the exit will leave TR
      displaying the normal replica of the host PC's display.


      APPENDIX C - Modem Cables

C1.   Minimum Standard Modem Cable

      Although a full 25-wire straight-through male-to-female RS232 cable is
      recommended for TeleReplica (since there is less room for error in the
      cable construction/selection), in fact the following signals are the only
      ones ever required or used:

      MALE (modem)                            FEMALE (PC)
      =============                           ========
      25D RS232 pin     signal       signal   25D   9D (as in AT)
      =============     ======       ======   ===   ==
                  2     TD  <------- TD         2    3
                  3     RD  -------> RD         3    2
                  4     RTS <------- RTS        4    7
                  5     CTS -------> CTS        5    8
                  7     GND <------> GND        7    5
                  8     CD  -------> CD         8    1
                 20     DTR <------- DTR       20    4
                 22     RI  -------> RI        22    9

      The following sections describe the kind of null modem cables that can be
      used with TeleReplica.

C2.   Simplest Possible 3-wire Null Modem Cable

      This is the most common kind of null modem cable, but TR and TRHOST must
      be set to ignore carrier detect, since the cable does not provide this
      information.

      MALE                                    FEMALE
      =============                           ========
      25D RS232 pin     signal       signal   25D   9D (as in AT)
      =============     ======       ======   ===   ==
                  7     GND <------> GND        7    5
                  3     RD  <------- TD         2    3
                  2     TD  -------> RD         3    2

C3.   Full TeleReplica Null Modem Cable

      If you can build or get hold of one of these, then TeleReplica can use
      carrier detect correctly. Note that CTS is not provided, and that
      TeleReplica must therefore be installed not to use it (there would be no
      point is using flow control with a direct cable in any case)!

      MALE                                    FEMALE
      =============                           ========
      25D RS232 pin     signal       signal   25D   9D (as in AT)
      =============     ======       ======   ===   ==
                  7     GND <------> GND        7    5
                  3     RD  <------- TD         2    3
                  2     TD  -------> RD         3    2
                 20     DTR -------> CD         8    1
                  8     CD  <------- DTR       20    4

C4.   Complete Null Modem Cable

      If you really want a complete null modem cable, which should work with
      ANY communications program, then I would suggest:

      MALE                                    FEMALE
      =============                           ========
      25D RS232 pin     signal       signal   25D   9D (as in AT)
      =============     ======       ======   ===   ==
                  7     GND <------> GND        7    5
                  3     RD  <------- TD         2    3
                  2     TD  -------> RD         3    2
                  5     CTS <------- RTS        4    7
                  4     RTS -------> CTS        5    8
                 20     DTR ----+--> CD         8    1
                                |
                                +--> DSR        6    6
                  8     CD  <--+---- DTR       20    4
                               |
                  6     DSR <--+


      APPENDIX D - DESQview Compatibility

D1.   TR is "DESQview-Aware" and runs nicely in a small DESQview window. TRHOST
      needs to put keys into the BIOS keyboard buffer, and this means that what
      is typed at the remote end cannot be distinguished by DESQview from what
      is typed at the real keyboard at the host end. The net effect is that
      there is no point in trying to run TRHOST in a DESQview window, and so
      TRHOST makes no attempt to be "DESQview-Aware". Also, DESQview is
      activated by "tapping" the ALT key, but TRHOST has no way to make this
      appear to happen, hence DESQview cannot be activated remotely. TRHOST and
      DESQview really don't mix!

D2.   For anyone wishing to set up DESQview for TR, these are the settings that
      I am currently using successfully:
      É1ÍÍChangeÍaÍProgramÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º                            Change a Program                           º
      º                                                                       º
      º Program Name............: TR                                          º
      º                                                                       º
      º Keys to Use on Open Menu: TR                  Memory Size (in K):  70 º
      ºÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄº
      º Program...: C:\TR\TR                                                  º
      º                                                                       º
      º Parameters: REMOTE                                                    º
      º                                                                       º
      º Directory.: \TR                                                       º
      ºÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄº
      º Options:                                                              º
      º               Writes text directly to screen.......: [N]              º
      º               Displays graphics information........: [N]              º
      º               Virtualize text/graphics (Y,N,T).....: [N]              º
      º               Uses serial ports (Y,N,1,2)..........: [1]              º
      º               Requires floppy diskette.............: [N]              º
      º                                                                       º
      º  Press F1 for advanced options           Press <ÄÙ when you are DONE  º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
      and advanced options:
      É1ÍÍChangeÍaÍProgramÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º                   Change a Program Advanced Options                   º
      º                                                                       º
      º System Memory (in K):  0    Maximum Program Memory Size (in K)..:  70 º
      º                                                                       º
      º Script Buffer Size:  100    Maximum Expanded Memory Size (in K):    0 º
      º                                                                       º
      º Text Pages: 1  Graphics Pages: 0  Initial Mode:  Interrupts: 00 to 2F º
      ºÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄº
      º Window Position:                                                      º
      º    Maximum Height: 25     Starting Height: 25     Starting Row...:  1 º
      º    Maximum Width.: 80     Starting Width.: 80     Starting Column:  1 º
      ºÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄº
      º                            Shared Program                             º
      º Pathname..:                                                           º
      º Data......:                                                           º
      ºÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄº
      º Close on exit (Y,N,blank)..: [Y]  Uses its own colors...........: [Y] º
      º Allow Close Window command.: [N]  Runs in background (Y,N,blank): [Y] º
      º Uses math coprocessor......: [N]  Keyboard conflict (0-4).......: [0] º
      º Share CPU when foreground..: [Y]  Share EGA when foreground/....: [Y] º
      º Can be swapped out (Y,N, ).: [N]  Protection level (0-3)........: [0] º
      º                                                                       º
      º  Press F1 for standard options           Press <ÄÙ when you are DONE  º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

D3.   When running under DESQview, the "shell to DOS" option during a file
      transfer is disabled, since DESQview does not permit interrupt handlers
      to call DOS and BIOS functions (necessary for reading and writing files).
      However, this is not a serious limitation under DESQview, since DESQview
      will allow you to run multiple simultaneous programs.

D4.   The normal "shell to DOS" option may be used under DESQview, but in this
      case more than 70K of memory will need to be allocated - with 4dos, it
      has been reported that at least 150K is required!


      APPENDIX E - Acknowledgements

      I would like to thank all the users of TeleReplica who have helped me to
      improve the package by suggesting new features and reporting
      difficulties. The following individuals in particular have had a
      significant impact on the current version:
            Mr Lindsay Smith, Monash University College, Gippsland, Australia
            Prof. Timo Salmi, University of Vaasa, Finland
==============================================================================
==============================================================================
==============================================================================
==============================================================================
==============================================================================
==============================================================================
==============================================================================
==============================================================================
==============================================================================
========================================================