Program GEODESIC for setting Waypoints in ATP
                              Version 1.0

                        (C) G. Berendt, 09/1992


Given the coordinates of two points in ATP, this program calculates the geo-
desic path (path of shortest length) between the points and displays the co-
ordinates of waypoints, which lie on the geodesic in equal distances. In ad-
dition to this, the program calculates the distances between the waypoints 
along lines, which cut the meridians under constant angles (Loxodromes) as
well as these angles.

The program can be used to set an arbitrary number of such waypoints for in-
stance along a route from the U.S.A. to Great Britain. As the magnetic devi-
ation within the ATP default scenery (or the East-scenery in IPS) a priori 
is not known and moreover does not smoothly change to the corresponding 
deviation in the Great Britain Scenery, the angles displayed are only a very
rough approximation to the measured ones and there will be a jump in the 
course at a longitude of about 45ø W.
Hence, you should only use the calculated angles as a guideline between those
two waypoints which lie on either side of the jump in the sceneries, because
it is only possible to set waypoints by menu F7, Option 5, within the same 
scenery. For this reason it is also recommended to choose two waypoints at 
least at approximately 46ø W and 43ø W longitude along the course.
With the precautions mentioned, it is possible to cross the Atlantic in ATP
with a B 747 or a B 767 without further difficulties.

Here follows as an example the outprint of the route file between the airports
of Boston, MA and Shannon, IR:


      Waypoints for the Route BOS - INN


Latitude 1:   42ø 21' 0"
Longitude 1:  71ø 0' 0"
Latitude 2:   52ø 42' 0"
Longitude 2:  8ø 56' 0"


Geodesic Distance: 2508.29 NM

-----------------------

Number of Sections: 8

Waypoint 1:

Lat[1]:                           45ø 18' 32"
Lon[1]:                           65ø  1' 49"

Geodesic Distance[1]:               313.54 NM
Constant Course Distance[1]:        313.60 NM
True Geographic Course Angle[1]:     55.50ø

Total Constant Course Distance:     313.60 NM


Waypoint 2:

Lat[2]:                           47ø 55' 27"
Lon[2]:                           58ø 26' 38"

Geodesic Distance[2]:               313.54 NM
Constant Course Distance[2]:        313.63 NM
True Geographic Course Angle[2]:     59.96ø

Total Constant Course Distance:     627.23 NM


Waypoint 3:

Lat[3]:                           50ø  7' 30"
Lon[3]:                           51ø 12' 56"

Geodesic Distance[3]:               313.54 NM
Constant Course Distance[3]:        313.66 NM
True Geographic Course Angle[3]:     65.09ø

Total Constant Course Distance:     940.89 NM


Waypoint 4:

Lat[4]:                           51ø 50' 13"
Lon[4]:                           43ø 22' 22"

Geodesic Distance[4]:               313.54 NM
Constant Course Distance[4]:        313.68 NM
True Geographic Course Angle[4]:     70.87ø

Total Constant Course Distance:    1254.57 NM


Waypoint 5:

Lat[5]:                           52ø 59' 27"
Lon[5]:                           35ø  0' 58"

Geodesic Distance[5]:               313.54 NM
Constant Course Distance[5]:        313.71 NM
True Geographic Course Angle[5]:     77.24ø

Total Constant Course Distance:    1568.28 NM


Waypoint 6:

Lat[6]:                           53ø 31' 57"
Lon[6]:                           26ø 19' 33"

Geodesic Distance[6]:               313.54 NM
Constant Course Distance[6]:        313.73 NM
True Geographic Course Angle[6]:     84.05ø

Total Constant Course Distance:    1882.01 NM


Waypoint 7:

Lat[7]:                           53ø 26'  1"
Lon[7]:                           17ø 32' 41"

Geodesic Distance[7]:               313.54 NM
Constant Course Distance[7]:        313.75 NM
True Geographic Course Angle[7]:     91.08ø

Total Constant Course Distance:    2195.76 NM


Waypoint 8:

Lat[8]:                           52ø 42'  0"
Lon[8]:                            8ø 55' 60"

Geodesic Distance[8]:               313.54 NM
Constant Course Distance[8]:        313.73 NM
True Geographic Course Angle[8]:     98.07ø

Total Constant Course Distance:    2509.49 NM

Actually, the jump between the US Scenery and the GB Scenery happens somewhere 
between Waypoint 3 and Waypoint 4. You should either divide that section once
more or use the given course until the jump has occured and then adjust it 
accordingly.


The author declines any responsibility for damages or inconveniencies the pro-
gram might cause; but you may use the program freely.
  
G. Berendt 

[CIS 100112,2506], [Internet: berendt@math.fu-berlin.de]