SKYMAP Version 3.6

                                   by

                               Rob Matson

Introduction
------------

SKYMAP is a menu-driven, high-precision celestial mapping program for gener-
ating star fields on an EGA/VGA monitor and/or an HP Laser Plotter (or any
similar hardcopy device that accepts the Hewlett Packard Graphics Language).
Polar, rectangular and stereographic map projections are supported, which can
be plotted at any scale and centered on any coordinate.  Stars can be plotted
for any epoch and any equinox, with defaults for Besselian 1950.0 (B1950) and
Julian 2000.0 (J2000).  Proper motion, precession, nutation, aberration, and
atmospheric refraction effects are all included.

In addition to stars, SKYMAP also plots the sun, moon and planets using the
equations of Jean Meeus to full precision.  The effects of parallax and light
travel time are included for all solar system bodies.  The positional accuracy
of the moon is ~10 arcseconds, while the sun's is better than 5 arcseconds.
With the exception of Pluto, planetary locations are accurate to around 10
arcseconds.  Pluto's positional accuracy is not known, but is better than
30 arcseconds between the years 1885 and 2099.

The user has the option of labeling the planets with their initial letters
(m,V,M,J,S,U,N,P) or their full names.  Additionally, the planets are color-
coded on the screen:  Mercury-dull red, Venus-cyan, Mars-bright red, Jupiter-
bright purple, Saturn-yellow, Uranus-green, Neptune-blue, and Pluto-dark
purple.  On the hardcopy, planets are plotted as unfilled circles in order
to easily distinguish them from the stars which are filled.

Although SKYMAP can be used simply to plot near-publication-quality celes-
tial maps, it's greatest feature is its ability to superimpose time-tagged
satellite trajectories.  Using a standard NASA 2-line element set, SKYMAP
can plot the trajectory of any low-earth orbit (LEO) satellite against the
stars as it would be seen from any location on or above the earth.  (SKYMAP
uses Space Command's SGP, SGP4 and HANDE algorithms, which are designed to
propagate the element sets of satellites with periods under 225 minutes. 
Since nearly all satellites that are visible to the unaided eye fall into
this category, the SDP4 deep-space routine has not been implemented.  SGP,
SGP4 and HANDE will still make predictions for "deep-space" satellites, but
with somewhat decreased precision.)

Similar to the way it handles satellites, SKYMAP also supports trajectory
plotting of rocket launches.  In this case, the 2-line ephemeris file is
replaced by a rocket trajectory file that contains a tabular listing of a
rocket's position as a function of time.  The format for each line of the
trajectory file is:  mission elapsed time (MET) in seconds, geodetic lati-
tude in degrees, longitude in degrees, and altitude in kilometers.  Negative
values are entered for south latitudes and west longitudes.  The MET values
need not be at regular intervals, but they must always increase.  SKYMAP will
cubically interpolate the rocket's position for intermediate times between
tabular entries.


Obtaining Satellite Ephemerides
-------------------------------

To achieve maximum satellite prediction accuracy, your ephemerides should
be as current as possible.  NASA two-line element sets can be found on the
Rancho Palos Verdes Bulletin Board System (RPV BBS), (310) 541-7299, oper-
ated by Dave Ransom.  These files are located in file area #4, are of the
form NASAxxx.TXT, and are updated approximately twice weekly in the PAK
compression format.  SKYMAP is also compatible with elements provided by
Ted Molczan on the Canadian Space Society bulletin board.  These elements
are updated weekly and also appear in compressed format in file area #4 of
the RPV BBS.  Their file names are of the form N2L-XXX.PAK.


Sun, Moon, and Planet Sizes
---------------------------

There are options to always plot the sun, moon and planets at their true
angular sizes, or to oversize them at low map zoom (map field of view greater
than ~15 degrees).  In the latter mode, the sun and moon are always plotted
at least 20% larger than Sirius, so that the full moon (which is plotted
white) can be distinguished from the stars, and the sun (plotted yellow) can
be distinguished from Saturn.  (If you were to plot a map with a 90-degree
field of view and true angular sizes, the sun and moon would appear as pin-
points.)  Keep in mind that when studying how a solar eclipse or planetary
transit will look, you should always use the true angular size setting.
Otherwise, the sun, moon and planets may appear oversized, leading to the
false impression that an eclipse or transit is occurring, when perhaps the
bodies are merely close to one another.


Differential Refraction
-----------------------

As of version 2.10, the effect of differential refraction on the appearance
of the sun and moon is modeled in SKYMAP.  This apparent "flattening" of the
sun and moon near the horizon occurs because the upper portion of the image
has not been refracted by as much as the lower portion, thus compressing the
image vertically.  SKYMAP includes differential refraction (in the stereo-
graphic projection only) for the sun and moon when their centers are less
than five degrees above the horizon.


Video vs. Hardcopy
------------------

Most of the labeling that occurs in the hardcopy also appears on the video.
This includes grid labels, map title, epoch and equinox, and planet and
bright star names.  However, because the video monitor resolution is not
nearly as good as that of a laser printer, satellite/rocket date and time
tags appear in the hardcopy only.  (The screen would be too cluttered other-
wise.)  Also, SKYMAP does not by itself create hardcopy output; instead, it
generates an HP-GL (Hewlett Packard Graphics Language) file which is compat-
ible with HP plotters such as the HP7475A.  With a rasterizing program such
as PRINTGL or Print-A-Plot, HP-GL files can be output on an HP LaserJet II or
similar printer.  (PRINTGL can be found on Dave Ransom's RPV BBS).  Due to
the large size of the HP-GL files that SKYMAP can produce (particularly for
maps plotted to magnitude 8.1), your laser printer must have at least a
megabyte of add-on memory to support plots at the full 300-dpi resolution.
If your laser printer has insufficient memory, you will have to reduce the
resolution to 150- or possibly 75-dpi in the rasterization program for the
file to be printed successfully.


Star Data Files
---------------

SKYMAP's star data files are based on the Smithsonian Astrophysical Obser-
vatory Star Catalogue (SAO), epoch B1950.  The SAO contains some 259,000
stars, but only those stars with visual magnitude brighter than 8.1 are
presently used by SKYMAP.  This 51,000+ star subset was first converted
from a 150-byte ASCII format to a 49-byte binary format for use with SKYMAP
1.2 and other astronomical software.  Later, the 49-byte format was further
condensed to a 28-byte per star format.  While the 49-byte format retains
all the information present in the original 150-byte ASCII source, the 28-
byte format contains only the right ascension, declination, visual magni-
tude and proper motion for each star.

Earlier versions of SKYMAP accepted both the 28-byte and 49-byte star file
formats.  However, since run times are cut by as much as 30 percent using
the 28-byte format, over a megabyte of disk space is saved, and modem
transmission time is reduced by 43 percent, SKYMAP no longer accepts the
49-byte format (as of version 2.5).  The 28-byte SAO catalogue can be found
in file area #6 of the RPV BBS.  This catalogue is stored in 22 separate
files, STARS01.DAT through STARS22.DAT, and has been compressed into 6
archive files, SMSTARS1.PAK through SMSTARS6.PAK.  Once downloaded and
unPAKed, you should have 22 files each containing 2350 stars, with the
exception of the last which has 1773.

Prior to version 2.5, SKYMAP would run using these 22 files with no further
modification.  However, in an effort to "clean up" disk directories, SKYMAP
now uses a SINGLE star datafile.  A program called BIGSTAR is provided in
file area #6 to concatenate the 22 files into a single star file.  This
program also gives you the option of filtering the catalogue to a desired
visual magnitude limit.  This way, if you are only interested in stars
through 6th magnitude, you don't have to carry the overhead of all 51123
stars (90% of which are dimmer than 6th magnitude).

A second program called P2000 is available in file area #6 to precess and
proper motion the SAO catalogue from B1950 to J2000.  SKYMAP will perform
precession and proper motion itself, but if you find that the majority of
the time you will want maps plotted for J2000.0, you should run P2000. 
This way, YOUR map epoch matches the star catalogue epoch, so that preces-
sion and proper motion are unnecessary when running SKYMAP.  This, of
course, accelerates the rate at which stars are plotted.

The precession and proper motion transformation does present a problem. 
Prior to transformation the catalogue is sorted by right ascension, but not
so afterward.  Precession to J2000 increases the right ascension of all
stars, which means that some stars which appeared toward the end of the
B1950 SAO catalogue will appear at the beginning of the J2000 catalogue. 
Furthermore, proper motion scrambles the order of the stars.  In order to
make use of a time-saving indexing scheme, SKYMAP expects its star file to
be in increasing order of right ascension.  For this reason a third program
called SORTSTAR is provided in file area #6.  This program uses a quicksort
algorithm, and can rapidly sort a file of up to 52000 stars.

For those users who don't need all the stars to magnitude 8.1, but would
prefer not to be bothered with running BIGSTAR, P2000 and SORTSTAR, I have
generated two ready-to-go files for your use.  MAG6.DAT contains all the
SAO stars through visual magnitude 6.0, precessed and proper motioned to
J2000.0, and sorted by right ascension.  This file contains all the stars
you are likely to see with the unaided eye.  For those with truly dark
skies, you may want to go to MAG65.DAT, which has all stars through visual
magnitude 6.5.  MAG6.DAT has 5093 stars, whereas MAG65.DAT has 9026.


Required Files
--------------

To plot satellite tracks with SKYMAP.EXE, you will need at least two aux-
iliary files in addition to the star catalogue and satellite ephemeris
files.  Most important is the configuration file discussed below.  The other
file you'll need is ASTROCLK.CTY (or any city file that uses the ASTROCLK.CTY
format).  This ASCII file allows you to quickly change sites knowing only the
site name (or any distinguishing substring of the site name).  Without this
file, you must type in the site latitude, longitude, altitude and timezone
each time you change sites.


Configuration File
------------------

The default name for the configuration file is SKYMAP.CFG, though SKYMAP can
run with any file name by typing "SKYMAP <configuration file name>".  (Don't
type the angle brackets).  If no file name follows "SKYMAP", SKYMAP assumes
SKYMAP.CFG is the configuration file.  If the configuration file is not found,
one will be created at run time, and default values will be assumed.

If you look at the contents of the default configuration file, SKYMAP.CFG,
you will notice that the format of each line is Parameter keyword = Value.
The parameter keyword assignments can be in any order, and SKYMAP recognizes
52 distinct keywords.  Not all keywords need to appear in the configuration
file; missing parameters will take on default values during program initial-
ization.  Keywords and values are not case sensitive, with the exception of
satellite names which are preserved by the program as they appear.  Many key-
words are logicals, which can only have the values TRUE or FALSE.  Actually,
the program will accept the words "TRUE", "ON" and "YES" synonymously.  All
other words are treated as FALSE.  The complete list of Keywords and their
defaults appears below.  The portion of any keyword in brackets is optional:

     Keyword    Default Value                     Notes
     --------   ----------------------- -------------------------
     STARFILE = MAG6.DAT
     CATEPOCH = J2000                   Others: B1950, MM/DD/YYYY
     CATJD = 2451545.0
     EPHEMFILE = NASA970.TXT
     CITYFILE = ASTROCLK.CTY
     SITENAME = Rancho Palos Verdes, CA
     LAT[itude] = 33.767501D0           (degrees, -90 to 90)
     LONG[itude] = -118.403334D0        (degrees, -180 to 180)
     ALT[itude] = 186.                  (meters)
     ZONE = -8                          (hours, -12 to 12)
     MAPTITLE = SkyMap Version 3.6
     EPOCHJD = 2451545.0
     EQUINOXJD = 2451545.0
     HPGLFILE = SKYMAP.PLT
     HPGL = OFF
     LABELSTAR = OFF
     LABELPLANET = OFF
     OCCULT = YES
     DRAWLAND = NO
     LANDFILES = <blank>
     PROPERMOTION = ON
     PRECESS[ion] = ON
     NUT[ATION] = ON
     LOCALSTART = TRUE
     LOCALTAG = TRUE
     TRUESIZE = FALSE
     EQOFDATE = TRUE
     EPOFDATE = TRUE
     TRACKRES[olution] = 10             (seconds)
     TAGRES[olution] = 30               (seconds)
     RA = 5.5                           (hours, 0 to 24)
     DEC[lination] = 0.0                (degrees, -90 to 90)
     DELRA = 10.                        (degrees)
     DELDEC[lination] = 10.             (degrees)
     MAXMAG[nitude] = 6.
     AZIM[uth] = 180.                   (degrees, 0 to 360)
     ELEV[ation] = 45.                  (degrees, -90 to 90)
     RFOV = 4.4                         (hours, >0 to 24)
     PFOV = 60.                         (degrees, >0 to 180)
     SFOV = 90.                         (degrees, >0 to 180)
     TRACKTYPE = EQUATOR[ial]           others: HORIZON
     PROJ[ection] = STEREO[graphic]     others: POLAR, RECT[angular]
     MODEL = SGP4                       others: SGP, HANDE
     PLOTMODE = STAR                    others: SAT[ellite], ROCK[et]
     SUNCODE = <not set>                others: ON, OFF
     MOONCODE = <not set>               others: ON, OFF
     SUNATSITE = <not set>              others: ON, OFF, AM, PM
     MAPDATE = <current date>           Format is MM/DD/YYYY
     MAPTIME = <current time>           Format is HH:MM:SS
     SATNAME(I) = <Satellite name>
     SATJD(I) = <JD of track start>
     SATDUR[ation](I) = 30              (minutes)

Some other notes: if you don't want a sun constraint on your satellites, do
not include the SUNCODE keyword in your configuration file.  The same applies
to MOONCODE (moon constraint at satellite) and SUNATSITE (sun constraint at
your site).  Also, SUNATSITE = AM means you are only interested in passes
that occur between midnight and sunrise; SUNATSITE = PM means you only want
passes between sunset and midnight.  The I in parentheses following SATNAME,
SATJD and SATDUR is the satellite index.  The index must be from 1 to 10, and
the parentheses are not optional.


Optional Files
--------------

If you wish to label bright stars with their common names, you will need the
ASCII text file STARNAME.TXT.  This file contains the names, right ascensions,
declinations, and visual magnitudes of 195 stars in alphabetical order.  The
first line of the file (2000.) is the epoch of the star coordinates.

SKYMAP also provides the capability to plot local geographical features with
your celestial maps (Stereographic projection mode only).  For example, local
mountains may obscure your horizon in a particular direction, blocking your
view of some celestial event.  If you have access to USGS topographical maps,
it is possible (although admittedly tedious) to construct mountain profiles
as seen from your site.  I recently used this very feature to rate viewing
locations in southern California for the January 4th, 1992, annular eclipse
at sunset.  SKYMAP showed me that Catalina Island would obscure many minutes
of annularity for coastal sites between Long Beach and Laguna Beach.  The
program allowed me to compare candidate sites so as to maximize my eclipse
viewing time.  CATALINA.PNT is included in this package as an example showing
the format of a geographical features file.  It is simply a list of survey
point coordinates (latitude, longitude, altitude in km) to be connected (in
order) with line segments.

Another application of this feature allows you to plot celestial views as
seen from a point well above the earth.  Thus, with a geographical feature
file containing continental boundaries, you could plot the earth and stars
as they appear from the Space Shuttle or Mir.  SKYMAP is compatible with
the CIA's World Database II .PNT files, which contain continental and poli-
tical boundaries as well as islands, lakes and rivers.  The seven WDB II
files are COAST1.PNT, COAST2.PNT, COUNTRY.PNT, STATE.PNT, ISLAND.PNT,
LAKE.PNT and RIVER.PNT.  For views above the western hemisphere, COAST1.PNT
is usually not needed (it contains coastlines for Asia, Europe and some of
northern Africa).  All of these files can be found on Dave Ransom's BBS.


File Summary
------------

To use all of SKYMAP's capabilities you should have seven or more files (not
including this .DOC file):

     1. SKYMAP.EXE
     2. Configuration file (def. SKYMAP.CFG)
     3. Star Catalogue file (def. MAG6.DAT)
     4. City file (def. ASTROCLK.CTY)
     5. Satellite ephemeris file (e.g. NASAxxx.TXT or XXX.N2L)
     6. STARNAME.TXT
     7. Geographical Features file(s) (e.g. COAST2.PNT, STATE.PNT, etc.)


Running SKYMAP
--------------

Type "SKYMAP" or "SKYMAP <configuration file>" from your DOS prompt.  If you
have prepared everything properly, something similar to the following messages
will appear on your screen:


          Reading configuration information from SKYMAP.CFG

          Total # of stars in MAG6.DAT:   5093
          Configuration information load successful.

                    Hit any key to begin


If the configuration file is missing, you will instead see the following:


          Warning: SKYMAP.CFG not found in current directory.
          Creating default configuration file.
          Reading configuration information from SKYMAP.CFG

          Total # of stars in MAG6.DAT:   5093
          Configuration information load successful.

                    Hit any key to begin


There is quite a bit of error checking during the configuration load se-
quence, with automatic recover procedures when at all possible.  In the
case of a missing star data file, you will get a message like the
following:

          Star datafile "MAG6.DAT" not found.
          Enter new star datafile name, or return to quit:

This allows you to use a star data file with a name different from that
which appears in the configuration file.


SKYMAP Menus
------------

SKYMAP is menu driven, which makes program operation very easy, even for
the beginner.  Once you get the message, "Hit any key to begin" following a
successful configuration load, you're all set to go.  Hit a key: the screen
will clear to a blue background, and SKYMAP's main menu will appear:

                              SKYMAP MAIN MENU

         F1  Star catalogue/epoch: MAG6.DAT [J2000]
         F2  Observer site: Rancho Palos Verdes, CA [ -8]
         F3  Date/time:  4/21/1992 12:00:00 Local
         F4  Map attributes: Az 180.00ø  Elev +45.00ø  FOV:  90.00ø
         F5  Plot mode: Star Map Only
         F6  HPGL Output File:  [None]
         F9  Display sun/moon/planet coordinates
         F10 Plot star map
         ESC Exit

The "F" numbers at the beginning of each line reference function keys on
your keyboard.  To select a menu item, type the function key associated with
that item.  The <ESCAPE> key, abbreviated "ESC" in the Main Menu, is used to
exit the program.  All other keys are ignored and will produce beeps when
typed.  The first four selections from the Main Menu call up submenus: F1
calls the Star Catalogue Menu, F2 calls the Observer Site Information Menu,
F3 calls the Date/Time Menu, and F4 brings up the Map Attributes Menu.  Each
of the these submenus will be discussed in turn, some of which also contain
submenus.


Plot Mode (Main Menu-F5)
------------------------

Function key F5 in the Main Menu is a plot mode toggle.  There are three
modes:  Star Map Only (the default), Satellite Trajectory and Rocket Trajec-
tory.  Very few of you will ever use the Rocket Trajectory mode, so I will
not discuss it here except to say that this mode can be used to plot the track
of a rocket (or any object for that matter) as it would be seen against the
stars from your particular viewpoint.  A rocket trajectory file is required
for this mode, and its format was described in the introduction.

The Star Map Only mode can be used if you don't want to overplot a satel-
lite trajectory.  In this mode, Main Menu functions F7 and F8 will not
appear.  In the Satellite Trajectory plot mode, functions F7 and F8 will
appear in the Main Menu:

                              SKYMAP MAIN MENU

         F1  Star catalogue/epoch: MAG6.DAT [J2000]
         F2  Observer site: Rancho Palos Verdes, CA [ -8]
         F3  Date/time:  4/21/1992 12:00:00 Local
         F4  Map attributes: Az 180.00ø  Elev +45.00ø  FOV:  90.00ø
         F5  Plot mode: Satellite Trajectory
         F6  HPGL Output File:  [None]
         F7  Satellite/rocket info  [ 0/ 0 loaded]
         F8  Set lighting constraints
         F9  Display sun/moon/planet coordinates
         F10 Plot star map
         ESC Exit


Star Catalogue Menu (Main Menu-F1)
----------------------------------

Hitting F1 in SKYMAP's Main Menu brings up the Star Catalogue Menu:

                             STAR CATALOGUE MENU

         F1  Star catalogue filename: MAG6.DAT
         F2  Star catalogue epoch & equinox: J2000
         F3  SKYMAP plot epoch: Ep of Date
         F4  SKYMAP plot equinox: Eq of Date
         F5  Proper motion: On
         F6  Precession: On
         F7  Nutation: On
         F8  Dimmest star magnitude:  +6.00
         ENT Return to Main Menu

F1 is used to change the star catalogue file.  F2 should be used to set the
star catalogue epoch & equinox to match that of the catalogue in use.  Star
catalogue files MAG6.DAT and MAG65.DAT are both J2000.  F3 is used to set
the epoch of the plot; this can be an actual date, or it can be flagged to
assume the date/time of the map as it is set in the Date/Time Menu.  In the
latter case, "Ep of Date" will appear in cyan instead of a date on the F3
line.  The plot epoch affects the positions of stars according to their
proper motions.  F4 is the same as F3 but with respect to equinox.  The plot
equinox affects the positions of all celestial objects and satellites since
it sets the direction of the celestial pole and the vernal equinox based on
precession.  Like the plot epoch, the plot equinox can be flagged to take on
the value of the current date/time as set in the Date/Time Menu.  In this
case, "Eq of Date" will appear in cyan instead of a date on the F4 line.

F5 through F7 are On/Off toggles for proper motion, precession and nutation.
Note that when proper motion is off, the plot epoch will assume the same date
as the star catalogue epoch/equinox.  Likewise, if precession is off, the plot
equinox will be the same as that of the star catalogue.  If the Nutation flag
is On, the effect of nutation will be applied to all celestial objects and
satellites.  Nutation is a slight, slow, nodding motion of the earth's axis of
rotation which is superimposed on the precession of the equinoxes.  In the
same way that the sun produces a torque on the earth's equatorial bulge causing
precession, the moon also produces a torque due to the earth's asphericity.
Since the moon's orbital plane precesses due to solar perturbation with a
period of roughly 18.61 years, the primarily lunar-caused precession (or
nutation) has this same period.  The magnitude of the nutation in longitude
never exceeds 19.3 arcseconds, and the magnitude of the nutation in obliquity
never exceeds 10 arcseconds.  Because the nutation effect is so small, it is
rare that you would ever need to have this flag on.  A map would have to be
highly zoomed to notice any screen difference between nutation on and off.
(Even a 2ø vertical field of view would show only a one pixel shift due to
nutation.)  Nutation is included primarily for those who want high-accuracy
celestial object positions in tabular form (Main Menu, F9).

Function F8 can be used as a dimmest star filter.  For example, if you were
plotting a daytime transit of the sun by a satellite, the stars would not be
visible.  By setting the dimmest star magnitude to -2, no stars would appear
on your plot.  Similarly, if you knew you would only be able to see the
brightest stars during a solar eclipse, you could set the filter at +1 or +2.


Observer Site Information Menu (Main Menu-F2)
---------------------------------------------

If you wish to change your current site (or just see its coordinates), enter
F2 to call up the Observer Site Information Menu:

                      OBSERVER SITE INFORMATION

         City File name: ASTROCLK.CTY
         Ground site name: Rancho Palos Verdes, CA
         Local Timezone Hour:  -8
         Site coordinates: Lat +33.7675ø  Long -118.4033ø  Alt  +186 m

         F1  Change City File name
         F2  Change ground site
         F3  Change site altitude
         F4  Change timezone hour
         F5  Add ground site to City File
         ENT Return to Main Menu

F1 is used to change the City file name.  To change ground sites, hit F2 and
then enter the name of the desired location.  SKYMAP will search your current
city file to locate the coordinates of your site.  Note that you do not have
to enter the entire city name, just enough to identify it.  SKYMAP searches
for matches, and with each match asks if it has found the city you want.  If
not, it continues searching until it has read the entire city file.  If your
city is not found, you will have to enter its latitude, longitude, altitude
and timezone yourself.  Remember that south latitudes and west longitudes are
entered as negative numbers, and altitude is in meters.  The timezone must be
from -12 to 12 and include the effect of daylight saving time if applicable
(e.g. -7 for California during daylight saving time).  Function F4 is helpful
in switching back and forth between standard time and daylight saving time
without having to change the ground site.  Likewise, F3 allows you to quickly
change your altitude independent of latitude and longitude.  (Site altitude
primarily affects the location of your physical horizon relative to your
zero-degree elevation angle.  It can also be used to produce geocentric
coordinates instead of topocentric ones by setting the altitude to coincide
with the earth's center: -6378135 meters at the equator.)  Once you've entered
a site's coordinates, you have the option of adding it to the City File using
function F5.


Date/Time Menu (Main Menu-F3)
-----------------------------

Use this menu to change the date, time, time type (local or UTC) and DeltaT:

                                 DATE/TIME MENU

                          F1  Map date:  4/21/1992
                          F2  Map time: 12:00:00
                          F3  Julian date: 2448734.333333
                          F4  Date/time type: Local
                          F5  Delta T:   58.26 secs
                          ENT Return to Main Menu

The time type is a toggle -- each time you hit F4, it changes between local
and UTC.  Note that the Date/Time and Julian Date are interrelated.  If you
change the Julian Date, the starting date and time change accordingly, and
vice versa.  Also, each time you use F1, F2, or F3, Delta T is recalculated.
(Delta T is the difference between UTC and Ephemeris Time, ET).  If you want
to use a particular Delta T, set the date and time first, THEN set Delta T
using F5.


Map Attributes Menu (Main Menu-F4)
----------------------------------

This is the menu you will be using most.  Here you control how the plot
will appear:

                              MAP ATTRIBUTES MENU

          F1  Map Type: Stereographic
          F2  Map Center: Az 180.00ø  Elev +45.00ø
          F3  Grid Spacing: RA  10.00ø  DEC  10.00ø
          F4  Vertical Field of View:  90.00ø
          F5  Star Map Title: SkyMap Version 3.6
          F6  Label planet initials
          F7  Sun/Moon/Planets: Oversized at low zoom
          F8  Occult objects below horizon
          F9  Land features Off
          F10 Edit land-feature file list
          ENT Return to Main Menu

F1 toggles the map type between Rectangular, Polar and Stereographic.  The
rectangular projection is appropriate when plotting portions of the celestial
sphere that are within 40 degrees of the equator; otherwise, a polar projec-
tion should be used as this will minimize distortion.  The Stereographic
projection is probably what you'll use the most since this shows you how YOUR
sky will appear.  With the Stereographic projection you control the azimuth
and elevation of the center of your plot, and the vertical field of view.
Azimuth is measured in degrees clockwise from north; thus, east is 90, south
is 180, west is 270 and north is 0.  Elevation is measured from 0 to 90, 0
representing the local horizontal (not necessarily the horizon), and 90 the
zenith.  As an example, if you want a view to the southwest that includes the
horizon and the zenith, you would set the azimuth to 225, the elevation to 45,
and the vertical field of view to 90.

Grid spacing (F3) controls the frequency of overlaid grid lines in right
ascension and declination for rectangular and polar plots, and azimuth and
elevation in the stereographic plot.  Values of 10ø or 15ø are good for
large fields of view.  I like to have between four and eight grid lines in
each direction, so I choose a round number grid spacing (1ø, 2ø, 5ø or 10ø
typically) that is four to eight times smaller than my field of view.  If
you want no grid at all, enter zeroes or negative values for the grid
spacing.  On the screen the grid appears cyan.  For the stereographic map
projection, a green local horizon line is also plotted.  (For sites at
sea-level, the horizon coincides with the zero-degree elevation line).

F4 is used to change the field of view of the plot.  For the rectangular
projection, you select the horizontal (right ascension) field of view in
hours; for the polar and stereographic projections you set the vertical
field of view in degrees.

F5 allows you to enter a title up to 70 characters long which will appear
left-justified below your map.  If you don't want a title, enter F5 and hit
return.

Functions F6 through F9 are all toggles.  F6 is a three-way toggle control-
ling how planets and stars are labeled in your plot.  The default is no star
labeling, and a single-letter planet label (m,V,M,J,S,U,N,P).  Hit F6 once,
and single-letter planet labels change to full names.  Hit F6 again, and
bright stars are also labeled with their common names (e.g. Polaris, Betel-
geuse, Rigel, etc.), provided that STARNAME.TXT is found in your directory.
Hit F6 a third time, and you're back to the default.

F7 toggles between "Oversized at low zoom" or "Actual size at any zoom".
Always use actual size when studying how solar eclipses and transits will
appear.  For large fields of view, you'll probably prefer the oversized
setting to more easily locate the sun and moon.

F8 toggles between showing objects below the horizon and occulting them.  Most
of the time you'll want to occult objects below the horizon.  An example of
when you might want to see objects below the horizon would be to verify that
the sun was down far enough after sunset or before sunrise to allow observa-
tion of a satellite pass.  Typically, the sun needs to be at least 8ø below
the horizon for good satellite seeing conditions.  (It is possible to acquire
Mir, the Space Shuttle, and occasionally the Hubble Space Telescope during
favorable passes when the sun is down only 5ø.)

F9 toggles land features on and off.  Unless you have a geographical features
file that you want overplotted on your map, leave land features off.  If you
have land features on, use F10 to enter the list of files that SKYMAP should
process (separate files with commas).  At plot time, any files in the list
that are not found by SKYMAP will be ignored.


HPGL Output Filename (Main Menu-F6)
-----------------------------------

Entering F6 from the Main Menu will pull up a small menu below it:

          F1  HPGL Output: Off
          F2  Filename: SKYMAP.PLT [New]
          ENT Return to Main Menu

F1 is an on/off toggle for HPGL file output.  If you don't need a hardcopy,
set output off as this will speed up program execution time.  Use F2 to
change the name of the HPGL output file.  The file's status [New] or [Exists]
will appear following the name.  When you return to the Main Menu, if the
HPGL file exists, a yellow message will appear following the name warning
you that the existing file will be overwritten when you plot.


Satellite Information Menu (Main Menu-F7)
-----------------------------------------

If the plot mode following F5 in the Main Menu is Satellite Trajectory,
you can call the Satellite Information Menu by hitting F7:

                         SATELLITE INFORMATION

F1  Ephemeris Filename: N2L-112.TXT          F6  Edit satellite list
F2  Trajectory resolution:   10 seconds      F7  Autolocate satellite pass
F3  Tag resolution:   30 seconds             F8  Special satellite commands
F4  Tag times: Local                         ENT Return to Main Menu
F5  NORAD model: SGP4

      #   Start Date/Time  Duration  Satellite Name
      1.  4/21/92 12:00:00  0:30:00  Mir Complex
      2.  4/21/92 12:00:00  0:30:00  Almaz 1
      3. 
      4.
      5.
      6.
      7. 
      8. 
      9.
     10.

With the exception of the lighting constraints which are set in the Lighting
Constraints Menu, all satellite parameters are set in the Satellite Informa-
tion Menu.  F1 allows you to change the name of the satellite ephemeris file,
usually of the type NASAxxx.TXT.  As mentioned before, Ted Molczan's N2L-XXX
format is also accepted by SKYMAP.

The Trajectory resolution (F2) tells SKYMAP how frequently to calculate the
satellite's position.  The shorter the time resolution, the longer it takes
SKYMAP to run, but the smoother the track will look.  Tracks are fairly
linear over 10-second periods, but if you are plotting a very small portion
of the sky you will want even more frequent positional information.  When
selecting the resolution, you should also be thinking about how frequently
you'll want the orbit time-tagged (set with F3).  Time-tags must occur at
some integer multiple of the trajectory resolution.  (Note that time-tags CAN
occur at every trajectory point if desired).  As an example, if a satellite
is going to take 30 seconds to cross your map, I would select a resolution of
1 second, and a timetag resolution of either 1 or 2 seconds.  Be careful not
to select so short a time between tags that they begin to overlap one another.
With a little practice, you'll get a feel for these time-related inputs.

F4 is a toggle between UTC and Local Time-tag labels.  This is independent
of the time type you've established in the Date/Time Menu.  For example,
your start date/time may be Pacific Daylight Time, but your time-tags can
be UTC if desired.


NORAD Propagation Model (Satellite Information Menu-F5)
-------------------------------------------------------

F5 is a toggle directing which propagation model to use, either SGP, SGP4
or HANDE.  Results will vary slightly depending on which model you use, but
should agree quite well with each other within a week of a satellite's
ephemeris epoch.  SGP is the lowest fidelity model, and consequently runs
the fastest.  SGP4 should theoretically give more accurate predictions, but
it takes slightly longer to run.  There will be negligible cross-track dif-
ference between SGP and SGP4, but the along-track position may differ by
several seconds depending on how "fresh" the orbital elements are.

The HANDE algorithm is the most sophisticated.  It was developed by Felix
R. Hoots for Air Force Space Command, Colorado Springs, Colorado, and first
appeared in Spacetrack Report #6 - Models for Propagation of Space Command
Element Sets, in July of 1986.  At that time, it was projected that in the
early 1990s all Space Command element sets would be generated with the
HANDE model, and that the element sets sent to external users would be pure
HANDE elements (in contrast to the current method of sending a mixture of
Brouwer and Kozai elements).  However, the last time I checked with Space
Command there was no near-term plan to make the switch.  I've included the
HANDE model in SKYMAP for the curious, and I would be interested in hearing
how it stacks up against SGP4 in terms of prediction accuracy.  For great-
est accuracy, HANDE needs special 17-element (3-line) ephemerides, but it
will run with 2-line elements, albeit with degraded accuracy.

As each call to any of these models involves hundreds of calculations, SKYMAP
utilizes a cubic interpolation scheme to speed up program execution.  Satel-
lite positions are calculated at two-minute intervals using the currently
selected NORAD model, and are cubically interpolated at intervening times at the
resolution set in F2.  Positional errors due to interpolation are no greater
than 60 meters for LEO satellites.


Edit Satellite List (Satellite Information Menu-F6)
---------------------------------------------------

Satellite names, start dates, times and durations are set in the Edit Satellite
Menu, which is brought up by entering F6 in the Satellite Information Menu:

                              EDIT SATELLITE MENU

              F1  Add satellite
              F2  Change satellite
              F3  Change start date
              F4  Change start time
              F5  Change duration
              F6  Delete satellite
              ENT Return to Satellite Menu

To add a satellite, enter F1.  If the satellite list is not already full,
SKYMAP will ask you to enter either a five-digit NORAD designation (e.g.
16609 for Mir), or a satellite name.  Numbers have an advantage over names
in that they are unambiguous, but names are easier to remember.  Selecting
satellites by name is similar to searching for a site name in the city file.
To find a particular satellite, SKYMAP does not need the whole name; just
enough of it to distinguish it from other satellites.  When SKYMAP finds a
match, it displays the full name of the satellite it has found, and gives you
the option of accepting it, or continuing to search for further matches.  If
no acceptable matches are found, SKYMAP will report "Name string not found.",
and ask you to enter another name or number.  To abort the search, just hit
enter for the name.

To change a satellite or satellites in the list, enter F2.  The following
message will appear:

         Enter satellite number(s) to change (1-10):

If you only wish to change one satellite, enter the index (1-10) of the sat-
ellite to change, and then just follow the normal instructions for adding a
satellite.  If you want to change several consecutive satellites, you can
save some key strokes by entering an index range.  For example, if you want
to change satellites 4 though 8, you would enter "4-8".

Functions F3-F5 are used to set the time segment that each satellite will
be propagated.  Upon adding or changing a satellite, the start date and time
are automatically set to your current map date and time, and the duration is
set to 30 minutes.  To change any of these values, use the appropriate func-
tion.  If you want several consecutive satellites to assume the same value,
you can enter an index range in the same way as above.

To remove a satellite from the list, use the delete function (F6).  Again,
you can either enter a single index # or an index range.


Autolocate Satellite Pass (Satellite Information Menu-F7)
---------------------------------------------------------

Plotting a satellite trajectory used to require a bit of preparatory work
BEFORE running SKYMAP, as SKYMAP did not have the "brains" to know when a
particular satellite was going to make a favorable pass over a given site.
A user had to first run a program such as Paul Traufler's TRAKSAT or Dave
Ransom's STSORBIT to know when and where a good pass would occur.  As of
version 2.9, SKYMAP will do this for you.  An analytical search function
has been added to the Satellite Information Menu under F7.  You provide
the search duration (in days) and the minimum elevation that the satellite
must exceed.  This search is subject to any lighting constraints you have
set.  (Lighting constraints are discussed later).  If you have loaded
multiple satellites, you must also provide the index number (1-10) of the
satellite to search on.  While the search is proceeding, a date counter
will appear to advise you of progress.  You can abort a search at any time
by hitting the escape key.

If no acceptable passes are found within the search duration, a message to
that effect will appear for a few seconds, and then control will return
to the Satellite Information Menu.  If a pass is found, the starting date
and time of the pass will be displayed along with the peak elevation.  (This
starting date and time will be three minutes before the satellite breaks your
horizon).  SKYMAP will automatically change the satellite's start date, time
and duration to correspond to the pass.  It will also remember the azimuth
and elevation of the peak of the pass in case you wish to use autopointing
later.  (Autopointing is handled in the Special Command Menu.)

This search function has been tested with many satellites from different
viewing locations, and seems to work well; however, the logic flow is very
tricky due to interaction with the lighting constraints, and it is possible
that the algorithm will have problems in particular situations.  If you run
across such a case, and your problem is repeatable, please let me know so
that I can work on a solution.


Special Satellite Commands (Satellite Information Menu-F8)
----------------------------------------------------------

At the present time there are three commands under the Special Command Menu:

                             SPECIAL COMMAND MENU

              F1  Automatic pointing
              F2  Track all satellites in file
              F3  Track coordinates: Equatorial
              ENT Return to Satellite Menu

F1 is used in conjunction with the autolocate function.  You can autopoint
to any satellite that has been previously autolocated.  If more than one
satellite is currently loaded, SKYMAP will ask for the index of the satellite
to be autopointed to.  If the satellite was successfully autolocated, SKYMAP
will set your map type to Stereographic (if it isn't already), change your
azimuth and elevation to correspond to the peak elevation of the pass, and
set your map date and time to correspond to the middle of the track duration.
For example, if the satellite's start time is 19:20 and its duration is 18
minutes, your map start time will be set to 19:29.

F2 is used to track ALL the satellites in your current ephemeris file.  You
supply the start date, time and duration, and SKYMAP will process the file
sequentially.  (Since this can take quite a while to run depending on the
length of your ephemeris file, you can discontinue the ephemeris file pro-
cessing at any time by hitting ESCAPE.)  All satellites are subject to the
lighting constraints you have set.

This command is useful if you are planning to take an extended exposure of a
region of the sky, and you want to know if any satellites are going to pass
through your field of view and "ruin" your photographic plate.  This feature
is also useful if you happen to spot an unexpected satellite passing through
a particular part of the sky.  By centering your map on the region of the sky
that the object passed through, and starting a search say 10 minutes before
the peak of the pass with a 20-minute duration, SKYMAP can tell you what it
was (assuming it's in the ephemeris file!)

F3 is a toggle between equatorial and horizon track coordinates.  Since the
stars, planets, sun and moon are plotted for a specific time, but satellite
tracks cover a range of times, there are two ways to plot the tracks.  If
you want the tracks to be correct relative to the stars, use equatorial track
coordinates (the default).  The horizon track mode is handy for planning long
photography sessions of multiple satellites using a single SKYMAP hardcopy.
In this mode, all satellite tracks appear at their proper instantaneous azi-
muth and elevation, but will not be correct relative to the stars except for
track times close to the map time.


Lighting Constraints Menu (Main Menu-F8)
----------------------------------------

Lighting constraints control what portions of an orbital track are plotted.
Functions F1 through F3 control toggles on the three different lighting
constraints:  sun at the satellite (F1), sun at the ground site (F2), and
moon at the satellite (F3).  For sun and moon at the satellite, F1 and F3,
the three possible conditions are Visible, Eclipsed, and No Constraint (i.e.
don't care).  As of version 2.10, there are five possible lighting conditions
at the ground site:  Day Only, Night Only, Sunset to Midnight, Midnight to
Sunrise, and No Constraint.  How these lighting constraints are set will
determine which satellite passes the autolocate function (F7 in the Satellite
Information Menu) will accept.  For example, if you don't like to get up for
those early morning satellite passes, hit F2 until the line reads "Sun at
ground site: Sunset to Midnight".


Display Sun/Moon/Planet Coordinates (Main Menu-F9)
--------------------------------------------------

This function was originally added for debugging purposes, but I found it
useful enough that I decided to add it as a feature.  If you want a tabular
display of the TOPOCENTRIC sun, moon and planet coordinates for your
selected site, date and time, just hit F9.  Note that through clever
selection of your site, you can display GEOCENTRIC coordinates instead.  In
the Observer Site Information Menu, select a site name that you know won't
be found in your City File (say "ZZZ").  When the unsuccessful search of
your City File is complete, SKYMAP will ask for the site coordinates.  Just
enter a latitude of zero, any longitude, and an altitude of -6378135 (the
equatorial radius of the earth in meters).  Your site is now the earth's
center!


Plot Star Map (Main Menu-F10)
-----------------------------

Once you've input all the necessary parameters and you're ready to plot,
hit F10.  If any satellite information needs to be loaded, brief messages
may appear at this time.  Then the screen will clear, a white rectangular
border will be appear with title, epoch and equinox labels, and a cyan grid
will be plotted (if the grid spacing is non-zero).  If in the satellite
trajectory mode, any visible satellite tracks will be plotted next in bright
red.  (While each satellite's track is being plotted, its name, NORAD desig-
nation, perigee, apogee and period will appear above the plot, along with a
percent completed indication.)  Once the satellites are complete, the sun,
moon and planets will be plotted (if they are visible), followed by the stars.
Once all stars are plotted, the bright stars' names will be added depending
on the setting of the label toggle under F6 in the Map Attributes Menu.

If land features are on, the land feature file list will be processed next.
As each file is read, its name appears above the plot.  Be warned that the
CIA WDB II .PNT files take a LONG TIME to process (with the exception of
STATE.PNT).  If you want to abort processing of the current land feature
file, hit ESCAPE, and SKYMAP will start on the next one.  Once all land
files have been plotted, the plot is complete and the message "Hit any key
to clear screen and goto Main Menu" will appear in green below the map.


Exiting SKYMAP (Main Menu-ESC)
------------------------------

Use the escape key in SKYMAP's Main Menu to exit the program.  (If you
should hit ESCAPE in the Main Menu by mistake, don't worry.  You must
confirm program exit.)  The program will then ask whether to save current default
parameters.  Hit "N" for no if you don't want to save your present
configuration.  The default is yes, and if you hit return, SKYMAP will ask
for the name of the file to save your configuration information in, with
your current configuration file in brackets.  Enter a file name, or hit
return to accept the default.  Program execution is then complete!


Problems
--------

The SKYMAP source code is over 11600 lines long, and as with anything of
this size, bugs can pop up.  If you experience a problem that seems to be
repeatable and can describe it clearly, please leave me a message on the
RPV BBS.  Sometimes it's just a user mistake.  For example, if a satellite
track isn't appearing that you know should be, check the search duration,
lighting constraints, the zone hour of your site, the time-type of your
time and date (UTC or local), and make sure you're looking in the right
part of the sky.

Bugs have been found by SKYMAP users before, and it is likely there are
more to be located.  Usually bugs crop up when significant features have
been added to a new version, and there have been over 3000 lines of code
additions/changes in the last two versions alone.


New Features
------------

I am always ready to listen to user's suggestions on improvements to SKYMAP.
In fact, many of the present features were suggested by current users.  Some
upcoming features under consideration include the addition of minor planets
and galaxies, a toggle to plot constellation line segments, and a special
function to search for satellite conjunctions with the sun, moon and planets.