CLOCK

                                     Version 3.31




                            CLOCK is a shareware program.
                     See Appendix A for registration information.






                       (c) Copyright 1991-1993 Ronald Q. Smith
































          CLOCK Version 3.31                               February 4, 1993


                                       CONTENTS



          1  INTRODUCTION . . . . . . . . . . . . . . . . . . . . . . .   2

          2  CLOCK.SYS - Replacement Device Driver  . . . . . . . . . .   5
               2.1  Unique Clock Hardware Support . . . . . . . . . . .   5
               2.2  Installing CLOCK.SYS  . . . . . . . . . . . . . . .   6
               2.3  Clock Type  . . . . . . . . . . . . . . . . . . . .  11
               2.4  Examples  . . . . . . . . . . . . . . . . . . . . .  13
               2.5  Future Enhancements . . . . . . . . . . . . . . . .  14

          3  CLK.EXE - Clock Control Program  . . . . . . . . . . . . .  15
               3.1  CLK Command . . . . . . . . . . . . . . . . . . . .  15
               3.2  Format of TZ= Function  . . . . . . . . . . . . . .  26
               3.3  Using CLK . . . . . . . . . . . . . . . . . . . . .  30
               3.4  Examples  . . . . . . . . . . . . . . . . . . . . .  33
               3.5  Errors  . . . . . . . . . . . . . . . . . . . . . .  34
               3.6  Future Enhancements . . . . . . . . . . . . . . . .  34

          4  CLKDEMO.EXE  . . . . . . . . . . . . . . . . . . . . . . .  36
               4.1  CLKDEMO Command Line  . . . . . . . . . . . . . . .  36

          5  IOCTL - API TO CLOCK.SYS . . . . . . . . . . . . . . . . .  37
               5.1  Data Structures . . . . . . . . . . . . . . . . . .  37
               5.2  clksta  . . . . . . . . . . . . . . . . . . . . . .  41
               5.3  setpw . . . . . . . . . . . . . . . . . . . . . . .  43
               5.4  connec  . . . . . . . . . . . . . . . . . . . . . .  45
               5.5  newpw . . . . . . . . . . . . . . . . . . . . . . .  47
               5.6  rstrct  . . . . . . . . . . . . . . . . . . . . . .  49
               5.7  stmode  . . . . . . . . . . . . . . . . . . . . . .  52
               5.8  stzone  . . . . . . . . . . . . . . . . . . . . . .  54
               5.9  tdisp . . . . . . . . . . . . . . . . . . . . . . .  58

          6  CLOCK.SYS - ASSEMBLY LANGUAGE API  . . . . . . . . . . . .  62
               6.1  Opening the CLOCK$ Device . . . . . . . . . . . . .  62
               6.2  Sending New Values to CLOCK.SYS . . . . . . . . . .  62
               6.3  Getting Current Status of CLOCK.SYS . . . . . . . .  64

          APPENDIX A:  DEFINITION OF SHAREWARE  . . . . . . . . . . . .  65
                                                                           








                                          2












          CLOCK Version 3.31                               February 4, 1993


          APPENDIX B:  CLOCK TYPES  . . . . . . . . . . . . . . . . . .  68
               B.1  Type 0 - PC/AT  . . . . . . . . . . . . . . . . . .  68
               B.2  Type 1 - Zenith Z-18x portables, Supersport 20  . .  69
               B.3  Type 2 - Various Zenith Data System PCs.  . . . . .  69
               B.4  Type 3 - Memory-Mapped Clocks . . . . . . . . . . .  70
               B.5  Type 4 - Direct Register I/O Bus Clock  . . . . . .  71
               B.6  Type 5 - Mitsubishi 8088 PCs  . . . . . . . . . . .  73
               B.7  Type 6 - Indirect Register I/O Bus Clock  . . . . .  74
               B.8  Type 7 - Complex I/O Bus Clock  . . . . . . . . . .  75
               B.9  Type 8 - Generic I/O Bus Clock  . . . . . . . . . .  77
               B.10 Type 9 - Quadram I/O Bus Clock  . . . . . . . . . .  77
               B.11 Type A - AT&T 6300, 6300 PLUS, 6300 WGS . . . . . .  78
               B.12 Type B - Hyundai 8088 clock . . . . . . . . . . . .  79

          APPENDIX C:  REVISION HISTORY . . . . . . . . . . . . . . . .  81



































                                          1












          CLOCK Version 3.31                               February 4, 1993


          1  INTRODUCTION

          CLOCK  consists of  two programs  that give you  complete control
          over the operation of your calendar (battery-protected) clock and
          your DOS/BIOS internal timer.   The normal DOS mode of  operation
          is to  read the calendar clock  when you boot the  system and set
          the internal timer.  Thereafter all read operations refer only to
          the internal timer  while time setting  operations write to  both
          clocks.  In levels of DOS prior to 3.3,  even time setting opera-
          tions only  wrote to the  internal timer.   In order  to set  the
          calendar clock you had to run the SETUP program.

          Some of the  drawbacks to the  standard DOS clock operation  that
          the CLOCK programs address are:                                  

               ù    There  is  no provision  to switch  time  zones without
                    resetting the system time.

               ù    DOS does not handle  automatic changes between daylight
                    savings time and standard time.                        

               ù    The DOS/BIOS internal timer  often drifts quite rapidly
                    away  from the  time maintained  by  the more  accurate
                    calendar clock.

               ù    Even  the calendar  clock drifts  slowly away  from the
                    accurate time.   DOS provides  no way to  automatically
                    adjust for that drift.

               ù    If your  battery is failing  or some other  hardware or
                    software  problem messes up  the time in  your calendar
                    clock, there is no way to detect that except by manual-
                    ly displaying the time and checking it.                

               ù    If you have to run a  program that occasionally changes
                    the time incorrectly,  there is no way  to protect your
                    clock  from those  changes.   You  can  also have  this
                    problem  if you  are a  parent whose  children  set the
                    clock when  you don't want them to, an instructor whose
                    students  reset the time, or an expert young user whose
                    parents mess up your clock.









                                          2












          CLOCK Version 3.31                               February 4, 1993


               ù    If you need to experiment  with special times and dates
                    but don't want  to have to reset your clock afterwards,
                    DOS has no mechanism to help.  In order to test end-of-
                    month processing for your application, you  have to set
                    the  date and time,  run your  tests, and then  set the
                    time and date back.

               ù    The standard DOS and BIOS software on some PCs can miss
                    the change  to a new  day when the  PC is left  on over
                    midnight.

               ù    Your clock  might not handle automatic changes to a new
                    year or may not understand leap years.

               ù    You may  have an older PC  from before the  PC/AT clock
                    standardization and your vendor no  longer releases new
                    versions  of DOS for that PC.  You are stuck on DOS 3.2
                    or earlier or you have to give up your calendar clock. 

          If any of  those circumstances cause problems for  you, CLOCK can
          help.   The two primary programs  are CLOCK.SYS and CLK.EXE.   In
          addition, if you are a software developer, CLKDEMO is provided in
          source code to show you how to program the extended  clock opera-
          tions into your own applications.                                


               CLOCK.SYS is a clock device driver (CLOCK$ device).  It
               replaces the DOS internal clock driver.  CLOCK.SYS pro-
               vides for  automatic time  zone  conversion.   It  also
               allows you to periodically or continuously get the time
               from the  calendar clock.   This can totally  eliminate
               problems with  missing day changes and  realtime clocks     
               that  are inaccurate.   CLOCK.SYS provides  support for
               many types  of calendar  clocks including  many of  the
               original add-in clocks of the  8088 era.  If your clock
               is not currently supported, I want to hear from you.  I
               will be happy to add it to the software.                    

               CLK.EXE  is  a program  that allows  you  to separately
               control your DOS/BIOS  internal clock and  battery-pro-










                                          3












          CLOCK Version 3.31                               February 4, 1993


               tected calendar clock.   Most importantly, CLK.EXE will
               handle time zones and will automatically switch between
               standard and  daylight savings time  for you.   It also     
               supports automatic adjustment for calendar clock drift,
               checks for  incorrect or  unlikely times,  and can  re-
               strict time changes.

               CLKDEMO.EXE is a small part of CLK.EXE that is provided
               in source  code (C language)  form so that you  can see     
               how to add clock control to your own applications.








































                                          4












          CLOCK Version 3.31                               February 4, 1993


          2  CLOCK.SYS - Replacement Device Driver

          CLOCK.SYS is  a device driver  that replaces the  built-in CLOCK$
          device driver in DOS levels 2.1  and above.  CLOCK.SYS adds  many
          functions not provided in the standard DOS CLOCK$ device  driver.
          You won't see mention of the DOS CLOCK$ device driver in your DOS
          user's  guides.  You will  see a very small mention  of it in the
          system's  programmers reference  manuals if  you are  an assembly
          language developer.   It  is there and  DOS was  specifically de-
          signed to let  you replace it  with one of  your own even if  the
          manual doesn't tell you that.


          2.1  Unique Clock Hardware Support
                                                                           
          CLOCK.SYS  was  originally written  especially  for  those people
          whose  clocks  are not  supported  by new  levels of  DOS.   This
          usually occurs  because your vendor stopped  providing new levels
          of DOS  adapted for your computer model.   Before the days of the
          PC/AT and standard clock interfaces, DOS was usually sold direct-
          ly to  hardware vendors  who customized it  for their  system and
          delivered it  with the system.   In  addition, many of  the early
          clocks were provided by third-party, after-market vendors who had
          no idea what system it would be used in.  Since those systems and
          clocks have been  out of production for a long  time, most of the
          vendors have stopped  providing upgrades.  Yet most  of those PCs
          will happily run  DOS 3.3 or above and especially  DOS 5.0 except
          that you have to give up your calendar clock.

          CLOCK.SYS supports a wide variety of different clock hardware and
          BIOS interfaces.  As far as possible, CLOCK.SYS will automatical-
          ly  determine what  clock  interface to  use.   If  the automatic
          determination  does  not  work  for  your  system,  you may  tell
          CLOCK.SYS specifically what interface type to use.   CLOCK.SYS is
          also required  by anyone  who  wants to  use CLK  as it  provides
          functions not  provided by the  normal DOS CLOCK$  device driver.
          CLOCK.SYS  is fully compatible with the  DOS device driver on all
          modern PCs and many older ones.
                                                                           
          If your PC clock is not currently supported but you would like to
          remove the  restrictions on  what versions  of DOS  you can  use,









                                          5












          CLOCK Version 3.31                               February 4, 1993


          please contact me by  mail or on CompuServe.  I  will be happy to
          add support for your clock.  I will need some  technical informa-
          tion and help from you in getting it to work so I will give you a
          $0  usage license for  your help.   Please see section  ? for the
          current list of supported clocks and Appendix B for a description
          of those clocks.


          2.2  Installing CLOCK.SYS


          To install the  device driver include the following  line in your
          CONFIG.SYS file.

          Syntax    device=[d:][path\]clock.sys [type][,io_addr]
                                                                           
                                          or

                    device=[d:][path\]clock.sys 3[,segment[,write0,
                         write1,read]]

                                          or

                    device=[d:][path\]clock.sys A[,base_year]


          Parameters     d:
                         Identifies the drive containing CLOCK.SYS.   If d:
                         is not provided, the boot drive is assumed.

                    path\
                         Specifies the directory  containing CLOCK.SYS.  If
                         path\ is not given, the root directory is assumed.

                    CLOCK.SYS
                         Is the name of the CLOCK.SYS file.  You may change
                         the name  if you  wish, but you  must not  use the
                         .COM or .EXE extensions.

                    type
                         Is the kind of calendar clock on  your system.  If
                         you do not provide type, CLOCK.SYS will probe your








                                          6












          CLOCK Version 3.31                               February 4, 1993


                         system   to  determine   which  clock   you  have.
                         CLOCK.SYS is  usually able  to detect the  type of
                         calendar clock  without trouble.   It is possible,
                         however, that you have some other hardware in your
                         system  that could fool CLOCK.SYS.   For that rea-
                         son, you might need to provide the type  of clock.
                         See  section ? and Appendix B for more information
                         about the clock types.


                    io_addr
                         Is the  I/O bus  address of  your clock  hardware.
                         Some  of the  types of  clocks that  are supported
                         were  set up at  a wide variety  of I/O addresses.
                         CLOCK.SYS probes  all the  commonly  used I/O  ad-
                         dresses  for these clocks.   However, you  or your
                         vendor may have installed your clock at an address
                         that CLOCK.SYS  doesn't know about.   By providing
                         the  address, you  make it  much more  likely that
                         CLOCK.SYS will correctly find your clock.  Even if
                         you  don't know what type  of clock you have, pro-
                         viding the I/O address may be enough for CLOCK.SYS
                         to determine which one it is.  io_addr is current-
                         ly  used with clock  types 4, 6,  7, 8,  9, and B.
                         Normally this is 240, 2C0, or 340 for types  4, 6,
                         and 7.  It is 210 or 310 for type 9.  And it is E0
                         for type B.  All numbers are in hex.  For example,
                         an AST Research clock might be:
                                                                           
                         device=[d:][path\]clock.sys 4,2C0

                         If  you do  not  specify the  "io_addr", CLOCK.SYS
                         will try to determine the correct address by prob-
                         ing.


                         If you are sure that you have an I/O clock but you
                         are not sure  which one it is, specify  type 8 and
                         supply the io_addr  if possible.  Type  8 does not
                         represent a specific clock.  Rather it attempts to
                         determine whether your clock is a type 4, 6, 7, 9,
                         or  B using a  sequence of tests  similar to those








                                          7












          CLOCK Version 3.31                               February 4, 1993


                         used by  some of the  I/O clock vendors  to figure
                         out what kind of clock you have.                  

                    If  you have  a memory  mapped clock,  you may  use the
                    second format  to specify the addresses to be used.  If
                    you don't know the addresses, CLOCK.SYS will attempt to
                    determine them by probing.

                    segment                                                
                         Is  the base  address  used to  access the  clock.
                         Usually your documentation  will give the  segment
                         address as four hex  digits such as FE00 or  F000.
                         Some addresses may be less than four digits (e.g.,
                         70).   Other  documentation may show  addresses in
                         the  form aaaa:bbbb.   In  this  case the  segment
                         address is  the aaaa value.   Sometimes these  ad-
                         dresses are  written as 0xaaaa,  aaaah, aaaaH,  or
                         0Xaaaa.  In all of these forms there is a 2- to 4-
                         digit hex number that is the segment address.

                    write0                                                 
                         Is the offset used to write  0 bits.  It must also
                         be a hex address  and may be 0, F002,  or anything
                         else the vendor chose.  If the addresses are given
                         in the aaaa:bbbb form, use  the bbbb.  With  these
                         clocks, you  read and  write the clock  by reading
                         the  memory addresses.   For example,  reading ad-
                         dress segment:write0 results in writing a zero bit
                         to  the clock.  Writing  an appropriate length se-
                         quence of zero and one bits sets the clock.

                    write1
                         Is the offset used to write 1 bits.


                    read
                         Is the offset used to read bits.

                         If  your documentation  gives the  segment address
                         but isn't  clear about  the offsets, just  specify
                         the  segment address  and CLOCK.SYS  will try  all
                         offset combinations that it knows about.








                                          8












          CLOCK Version 3.31                               February 4, 1993


                         If you specify one of the offsets, you must speci-
                         fy them all.

                    The third format is used with the AT&T 6300 clocks.

                    base_year
                         Is used for the AT&T 6300 clocks  (type=A).  Dates
                         prior to that year or more than 7 years after that
                         year will  not be handled  correctly.  If  no base
                         year is specified,  1992 will be used.   Dates be-
                         tween the start of  the base year  and the end  of
                         the seventh year later are handled (e.g., 1992-1-1
                         until 1999-12-31).

          Notes     DOS interfaces                    
                    --------------
                    All DOS  DATE and  TIME commands and  all DOS  date and
                    time system calls will  operate with no apparent change
                    to you  or any program.   Unless you  have used  CLK to
                    change the time handling, your  clocks are handled just
                    as DOS would handle them.

                    Dates and leap years                    
                    --------------------
                    CLOCK.SYS supports all valid DOS dates from 1980-1-1 to
                    2079-12-31.  It supports  dates to 2099-12-31 for  many
                    of the clocks.  CLOCK.SYS also handles year changes and
                    leap years automatically for  clock types that don't do
                    it themselves.           

                    Time zones and daylight savings time                    
                    ------------------------------------
                    CLOCK.SYS in conjunction  with CLK.EXE provides support
                    for multiple  time zones and  automatic conversion  be-
                    tween daylight  savings time and  standard time at  the
                    appropriate  times  of  the  year.   For  this  reason,
                    CLOCK.SYS may  be of  great  use to  you even  if  your
                    version of DOS already supports your clock correctly.

                    Clock synchronization                    
                    ---------------------
                    Normally,  CLOCK.SYS  operates identically  to  the DOS
                    CLOCK$ device  driver.  At  boot it sets the  DOS clock
                    from the calendar clock.  Any time  you change the date
                    or time it writes to both clocks.

                                          9












          CLOCK Version 3.31                               February 4, 1993


                    With CLK.EXE  you have several  other options.   If you
                    have  specified a  time zone  and offset  with CLK.EXE,
                    CLOCK.SYS will adjust  all times read from  and written
                    to the calendar clock by the time zone offset.  You can
                    also set  it to read the calendar clock rather than the
                    DOS  clock for  some  or all  time  requests to  ensure
                    continued synchronization of  the two clocks.   You can
                    also totally separate the  two clocks so that  DOS time
                    and  date functions  only read  and write  the DOS/BIOS
                    internal clock.

                    Time setting limits                    
                    -------------------
                    CLK.EXE  can tell CLOCK.SYS to apply limits to the time
                    changes that  it will  accept  or stop  accepting  time
                    changes at all.  For example, you can tell CLOCK.SYS to
                    accept no  changes that would  set the clock  backward.
                    You can also inhibit all changes.

                    Password Protection                    
                    -------------------
                    CLK.EXE can  establish  a password  to  control  future
                    changes to the time zone, connection, and  time setting
                    limits.   Once  the password  is  set, all  attempts to
                    change those values  will simply be ignored  unless the
                    correct password  is  supplied.   You  may  change  the
                    daylight versus standard time  flag and the  continuous
                    time display without knowing the password.             

                    Continuous Time Display                    
                    -----------------------
                    CLK.EXE can tell CLOCK.SYS to display the time continu-
                    ously at any position on your screen.   You specify the
                    cursor coordinates, display  attributes, and 12-hour or
                    24-hour  mode  and  CLOCK.SYS will  update  the display
                    every second.                                          

                    Saving Settings Across Boots                    
                    ----------------------------
                    With  CLK.EXE  you  can  save  the   current  state  of
                    CLOCK.SYS at  any time  in a form  that can be  used on
                    your next boot.  You can set up your time zone, setting
                    limits, connection mode, continuous display, and  pass-
                    word  and then save  a new version  of CLOCK.SYS.  This
                    new  version  will  automatically  start  running  with





                                          10












          CLOCK Version 3.31                               February 4, 1993


                    without having to scan for your clock type and with all
                    your standard state automatically in effect.           


          2.3  Clock Type

          There are almost as many  different implementations of PC  clocks
          as there are different types of PCs.  Until the PC/AT came along,
          there was no  standard for battery-protected clocks,  and each PC
          and add-in vendor was likely to implement them differently.  With
          the PC/AT a standard and documented interface for such clocks was
          provided.   Since  that time,  most PCs  have followed  the PC/AT
          standard.  It  is earlier  PCs, especially 8088  PCs, that  don't
          follow the standard.  Since these are early PCs, there  is also a
          high probability that the vendor is no longer  providing modified
          versions of  DOS with  built-in support for  their clocks.   Most
          add-in clock vendors never did provide a modified DOS and you had
          to  manage your  clock with  utility programs.   This  leaves you
          faced with  the choice between  staying with an early  version of
          DOS or giving up your clock.


          CLOCK.SYS is  intended to free  you from  those limitations.   It
          will  work with all  versions of DOS  from 2.10  through 5.00 and
          undoubtedly beyond.   It also attempts to automatically determine
          what kind of clock  you have and install the  correct support for
          it.  However, there are often enough differences between PCs that
          the automatic  determination may  not find  anything or  may even
          make the wrong choice.   To give you  more control of the  situa-
          tion, you may specify the  clock interface by giving an interface
          number.

          It will not  always be  easy to decide  what interface number  to
          use.   You will at least  need some technical information  on how
          your clock  works or on the  BIOS calls used to  control the bat-
          tery-protected clock.  If you find a description below that seems
          to match, give  it a try.  The most that  should go wrong is that
          your time and  date will be set incorrectly, but then they proba-
          bly weren't working anyhow.


          If you aren't sure what interface to  use or if you are sure that
          your clock is not supported, LET ME  KNOW.  I WOULD LIKE TO HELP.







                                          11












          CLOCK Version 3.31                               February 4, 1993


          You can help me make CLOCK.SYS better for everyone.  I would even
          like  to hear  from you if  CLOCK.SYS did  work for  you and your
          clock isn't  currently listed.   I would like  to be able  to add
          your PC manufacturer  and model number  to the supported  list so
          others know what to use.  If CLOCK.SYS did not work for you, I am
          interested in  making the changes so  that it does work.   If you
          can provide me with the  necessary technical information, I  will
          make the changes.


          Usually,  a technical  reference  manual with  hardware and  BIOS
          interfaces is the best source.  Even  if you don't have one, your
          original  hardware  vendor  may be  willing  to  send  you enough
          information to  allow you  to  program the  clock.   If all  else
          fails,  we may even be able to use  an old copy of DOS or a clock
          setting utility to figure out how  it works.  Before we do  that,
          check your license to be sure that it  is not forbidden to disas-
          semble the software to see how the clock works.  

          The following table  shows the systems that  have been determined
          to work  with existing  clock types.   If your  system is  in the
          list, try  the clock type indicated.  If not, look through Appen-
          dix  B which tells you about the  characteristics of each type of
          clock and see if anything seems to match your system type.


























                                          12












          CLOCK Version 3.31                               February 4, 1993



                           SYSTEM                 CLOCK TYPE


                   Amstrad PC1521DD        0 (May have to specify
                                           type to be recog-
                                           nized.)

                   AST Research            8 (4, 6, or 7)  See
                     Six-Pack              discussion above and
                     I/O Plus              in Appendix B.                  
                     etc.

                   AT&T 6300               A

                   Hyundai 8088            B

                   IBM PC/AT               0
                   and most PCs since
                   then.

                   Leading Edge Model D    5

                   Mitsubishi 8088         5

                   Quadram Corp.           9
                     QuadCard
                     QuadCard II
                     QuadCard 512+

                   SMT No-Slot Clock       3

                   Sperry PC-1             5

                   Sperry PC/HT            5

                   Tandy 1200HD            4

                   Vendex Turbo-888-XT     4

                   Zenith Supersport 20    1
                   Zenith Z-18x            1








                                          13












          CLOCK Version 3.31                               February 4, 1993


          2.4  Examples

          For almost everyone, the only format you ever need to use is:

               device=[d:][path\]clock.sys

          If CLOCK.SYS is in  the root directory of your boot  device, this
          is:
               device=clock.sys


          CLOCK.SYS will  quite happily load  into the upper  memory blocks
          (UMBs) provided by DOS 5.0 and by  other software.  With DOS 5.0,
          you might use:
               devicehigh=clock.sys

          With some  memory managers you can even load CLOCK.SYS into upper
          memory blocks on earlier levels of DOS.   See your manual for the
          commands to use.  Some of these  memory managers will create UMBs
          on 8088  and 80286 systems.   CLOCK.SYS  loads and  runs high  on
          those systems as well.

          With a memory mapped clock that uses an address combination  that
          CLOCK.SYS doesn't search automatically  and with CLOCK.SYS stored
          in the C:\UTILITY directory, you might use:
               device=c:\utility\clock.sys 3,ffff,f000,f004,f008
          Please note that the memory addresses chosen for this example are
          not likely to match those of your clock and you should substitute
          the addresses appropriate to your clock.


          If you have an  I/O clock with the same interface  as the Quadram
          Corp. clock but a different I/O address, you might use:
               device=clock.sys 9,3fc
          if your I/O base address were 3fc.


          If you have one of the AT&T 6300 system types and you occasional-
          ly need to set your clock prior to 1992-1-1, you might use:
               device=clock.sys a,1988

          2.5  Future Enhancements








                                          14












          CLOCK Version 3.31                               February 4, 1993


          Of course,  I hope  to add  more clocks as  people ask  for them.
          Those old PCs are still good for a lot of what we do even if they
          are sometimes relegated to a secondary status.                   

          There are no other outstanding enhancements currently planned for
          CLOCK.SYS.












































                                          15












          CLOCK Version 3.31                               February 4, 1993


          3  CLK.EXE - Clock Control Program

          CLK gives you complete control over the operation of the calendar
          clock  and DOS/BIOS  clock.  You  can operate  them separately or
          together.  You  can establish time  zones, daylight savings  time
          rules, automatic adjustment, synchronization rules, and more.


          3.1  CLK Command


          Syntax    clk [function] [function ...] [/I[file]] [/?]

                              or in full form

                    clk [A=ñsss.cc] [C=A|D|R|W] [D=[N][x,y,a[,12|,24]]     
                         [L=...] [R=A|B-hh:mm:ss|F+hh:mm:ss|N|R]
                         [S=C|D]  [TZ=...]  [W=-back,+forward]   [/I[file]]
                         [/P[N]] [/S[file]] [/?] [T?] [TZ=:?]

          Parameters     function
                         There are  many functions  that may  be used  with
                         CLK.EXE and  they are  discussed in  the following
                         paragraphs.  You  may use any number  of functions
                         on a  single command line  and they  will be  pro-
                         cessed  in  the order  in  which  you enter  them.
                         However, if any error is discovered  in any of the
                         functions, none of them are processed.  Thus,     
                              clk c=r tz=:est
                         is the same as the two command lines:
                              clk c=r
                              clk tz=:est
                         except that an error in either of the functions in
                         the first  example cause  the whole command  to be
                         ignored.

                         The case (upper  or lower) of any  of the function
                         names, options, or  values is  ignored except  for
                         the TZ function's  time zone names.   Even  there,
                         the case is not used.   It is simply preserved for
                         later display.









                                          16












          CLOCK Version 3.31                               February 4, 1993


                    none
                         If no function or option is provided, CLK displays
                         the current  state of operation  of CLOCK.SYS  and
                         the current time from both the  calendar clock and
                         the DOS/BIOS clock.

                         If you have used CLK to set a time  zone (TZ func-
                         tion), the current time zone name and offset value
                         are  displayed.     These  values  are  saved   in
                         CLOCK.SYS so that they may  be used for time func-
                         tions.

                         The connection state of the clocks (C function) is
                         displayed  as is the current restrictions (R func-
                         tion) on clock changes.


                         All  uses  of CLK  (except errors  and /?)  end by
                         displaying the  same information.  You always know
                         the state of your two clocks after execution.

                    A=ñsss.cc                                              
                         The Adjust function is used to set a daily adjust-
                         ment factor in seconds and 100ths of seconds.

                         This function assumes that you have some knowledge
                         of the  rate at  which your calendar  clock drifts
                         with respect to "real" time.   Presumably you have
                         periodically set your  clock using a  program that
                         calls the Naval Observatory or NIST and  noted the
                         difference  over  time.   Some such  programs will
                         help you to calculate the drift rate.  You can get
                         a very good adjustment from a decent quartz watch.


                         The value may be a positive or  negative number in
                         the range -326.99  to +326.99 seconds per  day but
                         reasonable values are likely to be a fraction of a
                         second.

                         The first time  you use A=, your clock  is not ad-
                         justed.  The value of  A and the current time  are
                         saved in  a file  for later  use.   Later you  can







                                          17












          CLOCK Version 3.31                               February 4, 1993


                         choose to run CLK with the /I option to invoke the
                         file.  The elapsed  time since the last adjustment
                         (or the time you last changed A) in days and frac-
                         tions is multiplied by A to  calculate any adjust-
                         ment that needs to be applied.  Only whole seconds
                         of adjustment are applied.

                         The A=  function only sets the  adjustment factor.
                         The  actual adjustment  is carried  out by  the L=
                         function.   You don't have  to enter the  L= func-
                         tion.  CLK will do that for you the first time you
                         use  A= and will  keep it up  to date  as it later
                         makes adjustments.

                         NOTE:   Do not use the  A= function with  the AT&T
                         6300 clocks (Type A)  or the Quadram clocks  (Type
                         9).  They  only permit the time  to be set to  the
                         nearest minute.

                    C=A
                         Connects  the two clocks for  All operations.  All
                         read operations go directly to the calendar clock.
                         The  calendard clock is read, the time is adjusted
                         for any time zone offset, and the adjusted time is
                         written to the DOS clock and returned to the call-
                         er.   With this function, your  calendar clock es-
                         sentially  becomes the only  clock.   However, the
                         DOS clock is set each time so that any application
                         reading the clock directly  (without going through
                         DOS) sees the same time  that DOS reports.  It  is
                         unwise  to use this function if your clock is slow
                         (some I/O clocks and some memory-mapped clocks) or
                         if it  only increments  in units of  seconds (most
                         clocks).  Any time zone offset is applied to reads
                         and writes.















                                          18












          CLOCK Version 3.31                               February 4, 1993


                    C=D
                         Disconnects  the two  clocks.   Any change  of the
                         date  and  time will  affect  the DOS  clock only.
                         Reads  also use the DOS clock only.  This function
                         allows you  to perform any  operation on  the time
                         without affecting  your  calendar clock.    It  is
                         useful for dealing  with ill-behaved programs that
                         need to change the  time and for testing  programs
                         at different dates  and times.  You  can later use
                         the C=R,  C=A, or other  functions to re-establish
                         the  value  in your  DOS  clock from  the calendar
                         clock.

                    C=R
                         Connects the  two clocks for writing  and periodic
                         Reading.    This function  may be  used  when your
                         clocks drift  slowly with respect  to each  other.
                         If  the time has not  been read for  about 10 sec-
                         onds, the calendar clock will be read, adjusted by
                         the offset if any,  and the adjusted time  written
                         to the DOS clock and returned to the caller.  This
                         periodic Read  assures you  that the  clocks never
                         get  very  far out  of  synchronization  with each
                         other.   Some  calendar  clocks take  a relatively
                         long  time to read  and most don't  have 100ths of
                         seconds.  By only  reading the calendar clock when
                         no other time request has  occurred in the last 10
                         seconds, we  minimize both  the  overhead and  any
                         visibility of time jumps.

                    C=W
                         Connects the two clocks for Writing.  This is  the
                         default  mode of  operation and  is the  same mode
                         that the DOS CLOCK$  device driver supports as its
                         only mode.   Reading the time is served by the DOS
                         clock.  Writing  the time sets both clocks.   If a
                         time  zone offset  has previously  been specified,
                         all  writes to the clock  are adjusted so that the
                         calendar  clock remains  on the  base  time.   For
                         example, if the  calendar clock is set to  UTC and
                         you specify that you want to use CST which has  an









                                          19












          CLOCK Version 3.31                               February 4, 1993


                         offset of 6 hours from UTC, all writes of the time
                         will have 6  hours added to them before writing to
                         the calendar  clock.  Thus  the DOS clock  and the
                         calendar clock remain at a constant time offset.

                    D=N
                         The  D= function  controls a continuous  time dis-
                         play.  D=N turns off the continuous display.


                    D=x,y,a[,12|,24]
                         Starts a continuous time  display at cursor  posi-
                         tion x,y with display  attribute a.  Cursor  posi-
                         tion 0,0 is  the upper left corner of  the screen.
                         The typical screen format runs from 0,0 to  79,24.
                         The display  attribute is  a two-digit  hex number
                         that  gives the background  and foreground colors.
                         The high-order digit is the background color (0 to
                         7 usually)  and the  low-order digit is  the fore-
                         ground or character  color (0 to F).   The default
                         display is a 24-hour  clock in the form  HH:MM:SS.
                         If you add  the ",12", the display will  use a 12-
                         hour clock.  No AM or PM indication is given.

                         D=72,24,79,12 will place the display at the  right
                         edge of the last line  of most screens.  The  text
                         will be in bright  blue on a white  background and
                         the hours will run from 12 through 11.


                    L=YYYY-MM-DD,hh:mm:ss,ñsss.cc                          
                         The L= function is not intended to be used on  the
                         command line,  but will be accepted if you provide
                         it.   The L= function  is normally created  by CLK
                         and  saved in the  CLK.INI file  for later  use in
                         processing adjustments.  The date  and time of the
                         last adjustment (or the most recent  time you gave
                         an A= function  on the command line)  are given by
                         the YYYY-MM-DD,hh:mm:ss.   Any non-digit except  a
                         space may separate  the sub-fields.  The  date and
                         time must be  followed by a comma and  any adjust-
                         ment  remainder.  The  adjustment remainder  is in








                                          20












          CLOCK Version 3.31                               February 4, 1993


                         the same form as the value for the A= function but
                         will usually be a fraction of a second.  It is the
                         adjustment that  was left  over the  last time  an
                         adjustment  was  actually  made  since  only whole
                         seconds of changes are made to the clock.

                         The  L= function triggers an adjustment if needed.
                         Generally,  it will  follow the  A= function  that
                         sets the  adjustment factor.  Both  of these func-
                         tions normally appear in the CLK.INI file.

                         The  L= function may also be  used by itself to do
                         simple  arithmetic on the  clocks.  Use  it on the
                         command line with any earlier date and time and an
                         adjustment of  the number of seconds  (positive or
                         negative) that you want added  to the clock.   The
                         change will  be made and the  last adjustment time
                         set to the current time.  For example, 
                              clk l=1990-1-1,0:0:0,-4
                         will subtract 4 seconds from the clocks.


                    R=A
                         The R= function sets restrictions on time changes.
                         R=A inhibits All time changes.  When this  mode is
                         set, all  attempts to change the  time are ignored
                         by CLOCK.SYS.  This  includes time changes attemp-
                         ted by CLK including time adjustments.  See R=N.


                    R=B-hh:mm:ss
                         This function limits the amount of Backward change
                         of the time.   Any change of more  than the speci-
                         fied time is  ignored.  The "-" is optional as are
                         the offset fields.                                
                              clk r=b
                         inhibits all backward changes.
                              CLK R=B::2
                         only  allows  backward changes  of two  seconds or
                         less This might permit CLK to perform  adjustments
                         but effectively stop other backward changes.









                                          21












          CLOCK Version 3.31                               February 4, 1993


                    R=F+hh:mm:ss
                         This function limits the amount  of Forward change
                         of the time.   Any change of more than  the speci-
                         fied time is ignored.  The "+" is optional  as are
                         the offset fields.
                              CLK R=F+1:00:02
                         limits  forward changes to  1 hour and  2 seconds.
                         The R=B and R=F  limits do not apply to  the auto-
                         matic  conversions between  standard and  daylight
                         savings time  as these don't  actually change  the
                         time.  The R=B and R=F functions are also indepen-
                         dent of the R=A function.

                    R=N
                         This function reverses the R=A function and inhib-
                         its No clock changes.   The R=A is independent  of
                         the R=B and R=F.  You can set backward and forward
                         limits with  R=B and R=F.   Later you  can inhibit
                         all changes with R=A.  When you do R=N, the previ-
                         ously set R=B and R=F limits again have an effect.


                    R=R
                         This function Resets the limits established by R=B
                         and R=F.  No limits are in effect  after executing
                         this function.  It has no effect on the R=A mode.

                    S=C

                         Sets both  clocks  to the  current  time from  the
                         calendar  clock.   You can  use this  even  if the
                         clocks  are  disconnected to  make  the  DOS clock
                         equal to the calendar clock.  The time zone offset
                         is  set to 00:00:00 and the  time zone name is set
                         to UTC to indicate that both clocks are set to the
                         base time.














                                          22












          CLOCK Version 3.31                               February 4, 1993


                    S=D
                         Sets both clocks  to the current time from the DOS
                         clock.  The value from the DOS clock is written to
                         the calendar clock.   The time zone offset  is set
                         to 00:00:00 and  the zone name  is not changed  to
                         indicate that both  clocks are set  to your  local
                         time.

                    TZ=...                                                 
                         Sets the DOS clock to the correct local time based
                         on the value of the  expression following the TZ=.
                         This  expression  conforms  exactly to  the  POSIX
                         1003.1  standard for time zone  handling.  CLK as-
                         sumes that the  calendar clock currently  contains
                         UTC (also  known as  GMT, Greenwich,  ZULU, and  Z
                         time).    UTC  ("Universal  Time,  Coordinated" is
                         usually spoken as "coordinated universal time") is
                         the name of the  international standard time  that
                         is provided  by WWV, WWVH, the  Naval Observatory,
                         and NIST as well as many other services around the
                         world.   Most  Unix(r)  systems  also  support  TZ
                         although many  only  partially support  the  POSIX
                         standard.   See  the notes  later  for a  complete
                         description of the TZ= function.

                         You  can  put  the  CLK  TZ=...  command  in  your
                         AUTOEXEC.BAT file.  You should put it prior to any
                         other statements that  may create or  update files
                         or  you run the risk  of having confusing times in
                         your  file directory  (MAKE  could get  especially
                         confused.).  If  you provide a TZ=  function, your
                         system  will automatically  adjust to  the correct
                         time zone every time  you boot.  Note that  no at-
                         tempt is made to change between daylight and stan-
                         dard time  except  when  you  execute  CLK  TZ=...
                         Adjusting on  the  fly is  very  dangerous.   Many
                         programs  can produce  incorrect  results or  even
                         corrupt your data if time takes a big step forward.
                         
--------------------
Unix is a registered trademark of Unix Systems Laboratories.









                                          23












          CLOCK Version 3.31                               February 4, 1993


                         and are  even more  likely to do  so if  time runs
                         backward.   See section ?  for a discussion of the
                         TZ= format.


                    W=-back,+forward
                         The W= function is used to establish Warning  lim-
                         its on  the time.   Each time  the W= function  is
                         processed  (usually  from the  CLK.INI  file), the
                         current time and  the previous time are  compared.

                         If the current time is outside the  -back,+forward
                         range around  the previous time, a warning message
                         is displayed  requiring you to  press a key.   The
                         program will  also exit with  an ERRORLEVEL  of 1.
                         The full form of the W= function is:
                         W=N-days/hh:mm:ss,+days/hh:mm:ss,                 
                              YYYY-MM-DD,hh:mm:ss

                         The  days sub-field is a value from 0 to 250 days.
                         The  days sub-field  combined with  the time  sub-
                         fields gives the maximum interval around  the pre-
                         vious  time  within which  the  current time  must
                         fall.   The previous date and time follow the sec-
                         ond comma.  For example,
                              clk w=-0/00:00:02,+91
                         will  establish a  range of  minus two  seconds to
                         plus 91 days.   The first time you  use this func-
                         tion nothing will happen except  that CLK will add
                         the current date and time to the command and store
                         it in the CLK.INI file.  The next time  you use if
                         from  the  CLK.INI file  with CLK /I,  the current
                         date and  time will  be compared  to the  previous
                         date and time  and the range.  If the current time
                         is outside  the range, a message  is displayed and
                         CLK pauses.

                         The sign characters and all of  the sub-fields are
                         optional.  Missing sub-fields are treated as zero.
                         The particular separators are not important except
                         for  the commas.   Any non-digit character  can be
                         used  for the other separators.  The time and date
                         fields are  appended to  the function by  CLK when







                                          24












          CLOCK Version 3.31                               February 4, 1993


                         the CLK.INI  file is written and  are the previous
                         time to which the next comparison will be made.  A
                         typical  function might  be  W=,31.   This command
                         will  display a  warning whenever  time  has moved
                         backwards at  all or  has moved  forwards by  more
                         than 31 days since the  last time you used CLK /I.
                         If you use CLK /I (see below) in your AUTOEXEC.BAT
                         file,  this is  very likely  to detect  a miss-set
                         clock or bad clock battery.  Yet it won't generate
                         a  message on  every boot.  You will  only get  an
                         "unnecessary" message if  it has been more  than a
                         month since you last used the PC.

                         If  the "N" character (or "n") appears immediately
                         after the "=", CLK does not pause and wait for you
                         to press a key after printing the warning message.
                         The "N" allows you  to use CLK in a .BAT  file and
                         check for the warning  with the IF ERRORLEVEL com-
                         mand.

                    /I                                                     
                    or
                    /Ifile
                         The I  option tells CLK  to read the  CLK.INI file
                         (or "file" if that  is given) for additional func-
                         tions.  These functions are usually A=, L=, and W=
                         functions that were previously written to the file
                         by CLK.  You  may add any other functions  (but no
                         options) to the file and they will be processed as
                         if you had entered them at the  end of the command
                         line.   If you  don't specify "file"  or you don't
                         give a path  as part of "file",  CLK will use  the
                         directory which  contains CLK.EXE.   Thus  the de-
                         fault  is to  use  CLK.INI in  the directory  that
                         contains CLK.EXE.  

                         If  you enter  an A=,  L=, or  W= function  or CLK
                         finds them in  the file, the file  will be updated
                         with the  new values  for  the current  time  when
                         appropriate.   If an  adjustment is  made, the  L=
                         function  will reflect  the date  and time  of the
                         latest adjustment.   CLK  will update or  create a








                                          25












          CLOCK Version 3.31                               February 4, 1993


                         CLK.INI file even  if you don't use  the /I option
                         if  you use  the A=,  L=, or  W= functions  on the
                         command line.


                         It is very useful to store your standard TZ=,  C=,
                         and  R= functions in the CLK.INI  file.  Then your
                         AUTOEXEC.BAT  file  can simply  contain  a CLK  /I
                         command  to set  your clocks  into their  standard
                         modes, adjust  the time,  and check for  bad clock
                         values.   You can also  reestablish your  standard
                         modes after  changes with the same command entered
                         from the DOS prompt or a .BAT file.

                    /P
                    or                                                     
                    /PN
                         Controls the  use of password  protection of  mode
                         changes.  When you use /P, CLK will ask  you for a
                         new password.  It will  then ask you to repeat the
                         password to ensure that you entered what you want.
                         It does  not display the password as you enter it.

                         The password is then passed to CLOCK.SYS and pass-
                         word  protection is enabled.   On future  calls to
                         CLOCK.SYS, you will be  asked for the password  if
                         protection is enabled.  You may use /PN to disable
                         password protection, but you  will have to provide
                         the  current password to do so.   If used with the
                         /S feature, the password protection will remain in
                         effect even across reboots.  /P should be the last
                         field on a CLK command line.

                    /S
                    or                                                     
                    /Sfile
                         Saves the current copy of  CLOCK.SYS as it resides
                         in memory.   If you  do not specify the  file, the
                         memory version is written to file CLOCK.NEW in the
                         same directory  that contains CLK.EXE.   While you
                         may  directly overwrite  the  file CLOCK.SYS,  you
                         should be very careful  doing so as whatever  your








                                          26












          CLOCK Version 3.31                               February 4, 1993


                         current state is will take effect on the next boot.

                         PLEASE  MAKE  A  BACKUP  COPY  of  your   original
                         CLOCK.SYS before replacing it  with a saved  file.
                         The  saved file  does not do  any probing  at boot
                         time as  it already knows exactly  what your clock
                         is.   It does not  need any parameters  on the de-
                         vice= line in CONFIG.SYS.


                         The /S  option may be extremely  useful for anyone
                         with multiple  similar systems  to maintain.   You
                         can set  up all of  your options  once on one  ma-
                         chine, save those with the /S option, and then use
                         the saved  file to  directly  install on  all  the
                         other machines.   If you use  password protection,
                         no  one  can change  the other  systems  except by
                         modifying  CONFIG.SYS  to  remove  the loading  of
                         CLOCK.SYS.

                         You  will still need  to run CLK  as part of every
                         boot operation (e.g.,  in AUTOEXEC.BAT) to  do any
                         automatic adjustment (A= and L=  functions), check
                         for clock failures (W= function), and check to see
                         whether the  clock should use the standard or day-
                         light offsets (TZ= function).  These functions are
                         not processed  automatically by  CLOCK.SYS because
                         they would increase the size  of the device driver
                         to an unacceptable limit.

                    /?
                         "/?"  or any error  will cause CLK  to display the
                         usage format.   If you have an error in any field,
                         CLK first displays that field.


                    T?
                         "T?" or any error in a TZ= function will cause CLK
                         to display the format of the TZ function.











                                          27












          CLOCK Version 3.31                               February 4, 1993


                    TZ=:?
                         "TZ=:?" or any error in a TZ= function that refers
                         to a pre-defined  time zone causes CLK  to display
                         all the  current pre-defined  time zone names  and
                         their associated values.


          3.2  Format of TZ= Function


          The format of TZ=... can get quite complicated as the standard is
          trying to  deal with  all time  zones and  daylight savings  time
          rules around the world.  The full format is:

               TZ=:zone
               or                                                          
               TZ=STD[offset][DAY[offset][,start[/time],end[/time]]]

          Parameters     zone
                         The form TZ=:zone  is the one you  are most likely
                         to need.   CLK knows the offsets and daylight sav-
                         ings time rules  for most of the U.S.  and all you
                         have to supply is the name of your time zone.  The
                         time zones currently known to CLK are:
                         EST  Eastern U.S. with automatic daylight
                         CST  Central U.S. with automatic daylight
                         MST  Mountain U.S. with automatic daylight
                         PST  Pacific U.S. with automatic daylight         
                         HST  Hawaiian with no daylight savings time

                         You can use CLK TZ=:? to display  the list of pre-
                         defined zone names and their values.

                         If you would like your favorite time added, please
                         send me the names, offset  from UTC, and any  day-
                         light savings time  rules that are  different from
                         the  U.S.  NOTE:  The names can be composed of any
                         characters except digits,  plus, minus, and comma.
                         They can be  up to  32 characters long.   Case  is
                         preserved in the  names only for later  display by
                         CLK.  You can call your zone MyZone.









                                          28












          CLOCK Version 3.31                               February 4, 1993


                         Case is not important  in matching the zone names.
                         tz=:cst is  the equivalent of TZ=:CST.   Both will
                         find the definition of CST.

                                  
                    You don't have to wait for me to modify CLK in order to
                    use your local rules or just try something out.  That's
                    what the long form is for.

                    STD                                                    
                         is any time  zone name for standard  time that you
                         want to use.  See the note above for the rules.


                    offset
                         is  the difference between your local time and UTC
                         and is expressed as hh[:mm[:ss]]  with an optional
                         leading + or -.  Offsets for times  West of Green-
                         wich are positive and those  East are negative.  A
                         24-hour  clock is  used  with  times running  from
                         00:00:00  to 23:59:59.    Mountain  Standard  time
                         would be expressed as:                            
                              TZ=MST+07:00:00
                                   or
                              TZ=MST7
                         and that's  what you would use if you live in Ari-
                         zona  and don't  want  any  daylight savings  time
                         adjustments.


                    DAY
                         is the  time zone name for  daylight savings time.
                         If you  don't use  daylight savings  time in  your
                         location, you should not supply this or any of the
                         following fields.


                         The offset for daylight  time is in the  same form
                         as  for standard  time.   If you  don't give  this
                         offset, it  is assumed to  be one hour  later than
                         standard time.  Thus a more complete specification
                         of the Eastern time zone would be:








                                          29












          CLOCK Version 3.31                               February 4, 1993


                              TZ=EST+05:00:00EDT+04:00:00
                                   or
                              TZ=EST5EDT4                                  
                                   or
                              TZ=EST5EDT     (since  daylight  is one  hour
                                             later by default)

                    start
                         is the day  of the year on  which daylight savings
                         time starts.  There are three formats that you can
                         use to give this day.  They are given below.

                    end
                         is the  day of  the  year on  which standard  time
                         starts again.   Note  that in  the Southern  hemi-
                         sphere it is quite possible for "end" to be earli-
                         er in  the year  than "start" as  daylight savings
                         time will include December and January.  end is in
                         the same  format as start.   Note from  the syntax
                         above  that you  must provide  end if  you provide
                         start.


                    time
                         is the  time of day  that the change  takes place.
                         It is in exactly the same format  as offset except
                         that leading  + and -  signs are not allowed.   If
                         you do not  specify the time, 02:00:00  is used as
                         the default.

          The day of the year form for start and end may be any of:

                    Jn
                         where n is a Julian day of the year from 1 to 365.
                         This form does not allow you to  refer to February
                         29.  Day  59 is always  February 28 and Day  60 is
                         always March 1.  This  is most useful in locations
                         where  a  particular calendar  date is  used every
                         year.











                                          30












          CLOCK Version 3.31                               February 4, 1993


                    n
                         where n is a Julian day of the year from 0 to 365.
                         This form  does allow you to refer to February 29.
                         January  1 is  day 0, February  28 is  day 58, and
                         either February 29 or March 1 is day 59  depending
                         on whether it is a leap year or not.  Not the most
                         useful  of forms but  it does deal  with locations
                         that might  specify February 29  as the date  that
                         time changes.


                    Mm.w.d
                         is used in places like the U.S. that do not speci-
                         fy a date,  but rather specify  a rule.  m  is the
                         month (1  to  12).   d  is  the day  of  the  week
                         (0=Sunday, 1=Monday,  ... 6=Saturday).   w  is the
                         week of the month (1 to  5).  Week 1 indicates the
                         first time that day d occurs in that  month.  Week
                         5 indicates  the last  time that  day d  occurs in
                         that  month whether  it is  the 4th  or 5th  time.
                         Thus the U.S. rule is
                              M4.1.0/02:00:00,M10.5.0/02:00:00             
                         or the first Sunday in April at 2AM until the last
                         Sunday in October at 2AM.

          The long form for Central U.S. time is:

               TZ=CST+06:00:00CDT+05:00:00,M4.1.0/02:00:00,M10.5.0/02:00:00
                         or
               TZ=CST6CDT5,M4.1.0/2,M10.5.0/2     (just leaving out zeros)
                         or
               TZ=CST6CDT,M4.1.0,M10.5.0          (since 2AM is default)
                         or
               TZ=CST6CDT                         (since  the U.S.  rule is
                                                  the default)


          3.3  Using CLK

          The most common use of  CLK will be to handle your  time zone and
          daylight savings time changes.  You need only do the following:









                                          31












          CLOCK Version 3.31                               February 4, 1993


          1.   Set your clocks to UTC.

          2.   Include the following line in your AUTOEXEC.BAT file.

                    CLK TZ=:zone   (where  you use  one of  the pre-defined
                                   zones)
                         or
                    CLK TZ=...     (where you define your own rules)

          That's it.  Everything else will take care of itself.  


          The only other time you will need to do anything is if you decide
          to correct your calendar clock to a more accurate time.  You will
          probably use  TIMESET or one of the  other programs that call the
          Naval  Observatory or NIST or maybe just your watch that you have
          set accurately.


          If you don't want to have to change the configuration of the time
          setting program,  you may want  to have it  always set UTC  or at
          least your local standard time.   If you want to have it  set UTC
          time, do the following:


               CLK S=C C=W
               run your time set program
               CLK TZ=...     (your normal TZ value)

          The C=W  in the first line  is only required if  you normally run
          with the clocks disconnected.


          Note that if you tell the time set program what your current time
          zone is, you don't have to do anything unless you have the clocks
          disconnected.

          Notes     Leaving your clock on local time                    
                    --------------------------------
                    If  you don't  want to be  bothered with  UTC, CLK will
                    quite happily work with your calendar  clock set to its
                    current value.    For example,  let's  assume that  you
                    currently have both clocks set to Pacific Standard Time
                    and you don't  really want to  be bothered changing  to
                    UTC, but you would like future changes between standard
                    and daylight  time to be  handled automatically.   Just
                    use the following statement in AUTOEXEC.BAT:



                                          32












          CLOCK Version 3.31                               February 4, 1993


                         CLK TZ=PST0PDT                                    
                    CLK believes whatever you tell it and will quite happi-
                    ly  operate assuming  that PST  is equal  to UTC.   You
                    could even  use CLK  with  your calendar  clock set  to
                    Pacific Daylight Time by using:
                         CLK TZ=PST1PDT

                    Avoiding missed days when your PC stays on all night,
                    and missed years and leap days on type 4 and 6 clocks                    
                    -----------------------------------------------------
                    If your PC is often left  on over midnight and seems to
                    miss the change to a new day, use:
                         CLK C=R TZ=...
                    in your AUTOEXEC.BAT file to have CLOCK.SYS periodical-
                    ly read the  time and date from the calendar clock.  If
                    your clock is  a type 4 or 6 clock  that doesn't update
                    years automatically and doesn't handle leap days,  then
                    this setting also ensures that  leaving your PC on over
                    the end of  a year or across February  29 doesn't cause
                    you to get the wrong date.


                    Using CLK.INI to simplify your commands                    
                    ---------------------------------------
                    If you always use  the same functions, you may  want to
                    edit the CLK.INI file that is included in this release.
                    You can include your TZ=,  C=, and R= functions in  the
                    file and just use:
                         CLK /I                                            
                    in your AUTOEXEC.BAT file.

                    Adding and subtracting time                    
                    ---------------------------
                    You can pretty much do anything including simple arith-
                    metic on  your clocks  by  using the  functions in  the
                    correct sequence.   Let's say that  you want to add  12
                    hours  to the current  time in both  clocks because you
                    inadvertently  set  AM time  instead of  PM time.   The
                    following function sequence will do that:
                         CLK TZ=Igoofed-12 S=D TZ=:pst                     
                    The TZ=Igoofed-12  (or use any other name for the zone)
                    sets your DOS clock to 12 hours later than the calendar
                    clock.  (Yes, I know that time zone offsets seem  back-







                                          33












          CLOCK Version 3.31                               February 4, 1993


                    wards since you  subtract them from the  base time, but
                    that's the way the official standards have them.)


                    The S=D sets  both clocks to the value in the DOS clock
                    with a zero offset.

                    The  TZ=:pst should be replaced by whatever your normal
                    TZ  function is or even by a  /I to pull in your normal
                    settings.

                    If you normally have your clocks disconnected, insert a
                    C=W function as the first function.

                    Correcting inadvertent problems                    
                    -------------------------------
                    Just remember that except for the S=D function, CLK and
                    CLOCK.SYS  always  start with  the assumption  that the
                    calendar clock is  the base and  do all their  calcula-
                    tions  from that point.  Thus  you can play with TZ and
                    other functions as much as you want and always get back
                    to your normal local time just by  using your normal TZ
                    command.  The calendar clock will not have been affect-
                    ed unless you  did something to set  the time or  date.
                    You can avoid  even that problem by  disconnecting your
                    clocks  (C=D) or  restricting time  changes (R=A).   In
                    fact, if you have trouble with some  program messing up
                    your clocks, try the following:


                         CLK C=D
                         execute program
                         CLK S=C C=W (or C=R) TZ=...  (your normal)

                    If you  have your standard  C= and  TZ= functions in  a
                    file, you can simplify this as:                        

                         CLK C=D
                         execute program
                         CLK S=C /I

                    You  may even  want to  make up batch  files containing
                    this sequence  to run those troublesome programs.  Some
                    games are major causes of problems because they set the






                                          34












          CLOCK Version 3.31                               February 4, 1993


                    DOS  clock  running faster  or  slower  than normal  to
                    control the pace of the game.  As long as  they restore
                    the normal rate when they exit, the above sequence will
                    eliminate any clock drift problems.

                    Fast DOS clock drift                    
                    --------------------
                    Some high-speed communication  programs will also cause
                    the DOS clock  to run slow by causing  the BIOS to miss
                    clock interrupts.   Fortunately, a C=R function  should
                    virtually eliminate problems of this type.


          3.4  Examples

               clk A=0.34                                                  
                    sets an adjustment factor of 0.34 seconds per day.  The
                    A=0.34  function will  be written  to the  CLK.INI file
                    along with an L=  function with the current time  and a
                    zero remaining adjustment.  Every time thereafter, that
                    CLK is run with  the /I option, it will check to see if
                    it is  time to  adjust the clocks.   About  every third
                    day, it will add 1 second to both clocks.

               clk s=c /i
                    sets the DOS clock to  the current calendar clock  time
                    without any time  zone adjustment.   The /i causes  all
                    functions in the  CLK.INI file to be added.   If one of
                    them  is a tz function, we have corrected the DOS clock
                    for any changes  made to it and re-established our time
                    zone.  This is a good command line to use following a 
                         clk c=d
                    and other operations that may have led to an  incorrect
                    time in the DOS clock.


               clk c=r tz=:est r=b-00:00:02 r=f+00:00:02
                    sets CLOCK.SYS to read  the calendar clock about  every
                    10 seconds  and re-synchronize the  DOS clock  with it;
                    applies the appropriate Eastern time zone (standard  or
                    daylight depending on date);  and prohibits changes  to
                    the clock of more than 2 seconds in either direction.








                                          35












          CLOCK Version 3.31                               February 4, 1993


          3.5  Errors

          When errors are detected, CLK prints a message.  It also sets the
          ERRORLEVEL on each program termination as follows:

          0    Normal termination or only warning messages.

          1    Time outside warning range.  Warning issued.                

          2    Error in command line or CLK.INI file  functions.  The func-
               tion with the error is displayed followed by the appropriate
               usage rules.

          3    Internal error or system error (e.g., unable to open  handle
               to CLOCK.SYS).



          3.6  Future Enhancements

          Several enhancements are planned for future releases of CLK.


               -    New  functions for CLK  or a companion  program to help
                    calculate  the  time  adjustment  factor  (A=  function
                    value).    You would  provide input  on  the difference
                    between  the correct time  and the  current time.   You
                    might get  this from  a good watch  or by  running your
                    favorite Naval  Observatory/NIST dialer  program.   CLK
                    will save these differences and the  current time until
                    it had enough  information to give you a new adjustment
                    factor.   By  having CLK  or a  related program  do the
                    calculations,  it  can  automatically account  for  the
                    adjustments  that  you are  already doing  with  A= but
                    which aren't quite accurate enough.


               -    Full  screen interface that displays the current status
                    of all the things that  CLK and CLOCK.SYS know and lets
                    you change them just by editing the screen.  The rather
                    clunky command line  interface needs to  remain as  its
                    compact function  definitions are  what you  want in  a
                    .BAT file.







                                          36












          CLOCK Version 3.31                               February 4, 1993


          4  CLKDEMO.EXE

          A simple version of the CLK  program, called CLKDEMO, is provided
          in both  executable and source code form.   CLKDEMO only provides
          support for the C= functions and displaying the clock status.  It
          is included  to show you  how to add  clock handling to  your own
          applications.   CLKDEMO  is  written in  C and  is  compiled with
          Microsoft C 5.1.



          4.1  CLKDEMO Command Line

          Syntax    CLKDEMO [C=A|D|R|W] [/?]

          The functions provided work exactly as  they do in CLK.   CLKDEMO
          also displays the status and the current times.

          Since  CLKDEMO.EXE is merely a subset of CLK.EXE, it isn't terri-
          bly useful as a utility in its own right.  Its value is that  the
          source code  is  provided.   There are  three  source code  files
          provided.   CLKDEMO.C  is the  main program and  performs command
          interpretation and execution.  IOCTL.C is a set of functions that
          read  and  write the  CLOCK$ device  driver  using the  DOS IOCTL
          functions.  IOCTL.H  is a set  of definitions which  are used  by
          CLKDEMO and IOCTL.C.
























                                          37












          CLOCK Version 3.31                               February 4, 1993


          5  IOCTL - API TO CLOCK.SYS

          IOCTL  is provided to allow you to build your own applications to
          use  the additional functions that CLOCK.SYS provides.  There are
          several  APIs  (Application Programming  Interfaces)  provided as
          part of  IOCTL.  These  APIs are sufficient to perform all of the
          extended functions.

          All of  the APIs  are defined  to be directly  callable from  all
          Microsoft  compatible languages including  MASM, FORTRAN, Pascal,
          and BASIC.   Languages other  than C  refer to the  API names  as
          upper case characters.  Object code versions are provided for the
          small, medium,  and large  memory models.   These  may be  linked
          directly with your  applications.  The  object code versions  are
          SIOCTL.OBJ, MIOCTL.OBJ, and LIOCTL.OBJ for the small, medium, and
          large models respectively.


          5.1  Data Structures

          Data structures are defined in ioctl.h that are used in the calls
          to the IOCTL functions.


            /* "modes" holds flags that control the operation of CLOCK.SYS   */

            struct modes {
                unsigned : 9;                                              
                unsigned day_light: 1;
                unsigned disp_24 : 1;
                unsigned disp_tim : 1;
                unsigned pw_ena : 1;
                unsigned disabl : 1;
                unsigned chk_forw : 1;                                     
                unsigned chk_back : 1;
            };














                                                  38












            CLOCK Version 3.31                               February 4, 1993


            /* "off" holds a time offset in hours, minutes, and seconds.   */

            struct off {
                int hour;                                                    
                int minute;
                int second;
            };

            /* "date_time"is a structure that holds a date and time.      */


            struct date_time {
                int year;
                int month;
                int day;
                struct off time;
                int hsecond;                                                 
            };

            /* "time_zone" holds a time zone name and offset.          */

            struct time_zone {
                struct off offs;                                             
                unsigned char zone[32];
            };

            /* "limit" is used to hold the data that sets time limits for 
               changes.  */

            struct limit {                                                   
                struct off back;
                struct off forward;
            };

            /* "disp" is used to hold the data that specifies the location 
               and attributes of the continuous time display.             */

            struct disp {
                int x;
                int y;
                int attribute;
            };








                                                  39












            CLOCK Version 3.31                               February 4, 1993


            /* CLOCK_DATA is the CLOCK.SYS data that is returned by clksta
               (AKA CLKSTA for FORTRAN, Pascal, and BASIC languages).  
               Because we need to be language independent, all of the data
               is word-aligned. Only the data types int and character are
               used. Some of the int data is encoded bits or addresses. */

            struct CLOCK_DATA {
                int connected;               /* Connection state     */
                struct modes mode;           /* Mode bits           */
                struct date_timecal_time;    /* Current date and time */
                struct time_zone standard;   /* Offset of standard UTC */
                struct time_zone daylight;   /* Daylight offset      */
                struct limitrules;           /* Maximum clock movement */
                structdisp display;          /* Time display loc and attr*/
                unsignedchar vers[6];        /* CLOCK.SYS version nnn.nn*/
                int clock_type;              /* Type of clock installed */
                int ct_1;                    /* Data for clock type    */
                int ct_2;
                int ct_3;
                int ct_4;
                unsigned intclock_seg;       /* Segment CLOCK.SYS loaded at */
                unsigned int clock_long;     /* Size of CLOCK.SYS          */
            };


          This data structure is treated as the following integer  array in
          the FORTRAN and BASIC languages.

          BASIC          
          -----
               OPTION BASE 1
               DIM CDATA(66)

          FORTRAN          
          -------
               INTEGER*2 CDATA(66)


          ARRAY INDEX         CONTENTS                 STRUCTURE ELEMENT          
          -----------         --------                 -----------------
          CDATA(1)       =    Connection state         connected
          CDATA(2)       =    Mode bits                mode
          CDATA(3)       =    Year from calendar clock cal_time.year
          CDATA(4)       =    Month                    cal_time.month   
          CDATA(5)       =    Day                      cal_time.day
          CDATA(6)       =    Hour                     cal_time.offs.hour




                                          40












          CLOCK Version 3.31                               February 4, 1993


          CDATA(7)       =    Minute                   cal_time.offs.minute
          CDATA(8)       =    Second                   cal_time.offs.second
          CDATA(9)       =    100th of second          cal_time.hsecond 
          CDATA(10)      =    Standard hours from UTC  standard.offs.hour
          CDATA(11)      =    Standard minutes         standard.offs.minute
          CDATA(12)      =    Standard seconds         standard.offs.second
          CDATA(13) -                                  standard.zone
          CDATA(28)      =    Standard time zone LJSF
          CDATA(29)      =    Daylight hours from UTC  daylight.offs.hour
          CDATA(30)      =    Daylight minutes         daylight.offs.minute
          CDATA(31)      =    Daylight seconds         daylight.offs.second
          CDATA(32) -                                  daylight.zone
          CDATA(47)      =    Daylight time zone LJSF
          CDATA(48)      =    Maximum hours backward   rules.back.hour
          CDATA(49)      =    Maximum minutes backward rules.back.minute 
          CDATA(50)      =    Maximum seconds backward rules.back.second
          CDATA(51)      =    Maximum hours forward    rules.forward.hour
          CDATA(52)      =    Maximum minutes forward  rules.forward.minute
          CDATA(53)      =    Maximum seconds forward  rules.forward.second
          CDATA(54)      =    x cursor position        display.x
          CDATA(55)      =    y cursor position        display.y           
          CDATA(56)      =    attribute                display.attribute
          CDATA(57) -                                  vers
          CDATA(59)      =    CLOCK.SYS version LJSF
          CDATA(60)      =    Clock type               clock_type
          CDATA(61)      =    I/O address, base memory ct_1
                              segment, or base year                        
          CDATA(62)      =    Read memory offset       ct_2
          CDATA(63)      =    Write-0 memory offset    ct_3
          CDATA(64)      =    Write-1 memory offset    ct_4
          CDATA(65)      =    Segment address          clock_seg
                              where CLOCK.SYS is loaded
          CDATA(66)      =    Length of CLOCK.SYS      clock_long

















                                          41












          CLOCK Version 3.31                               February 4, 1993


          5.2  clksta

          þ  Summary


          C          
          -

          #include <ioctl.h>

          extern int pascal far clksta(struct CLOCK_DATA *cdata);

          BASIC          
          -----

          OPTION BASE 1
          DIM CDATA(66)

          DECLARE FUNCTION CLKSTA%(BYVAL Addr AS INTEGER)

          STATUS% = CLKSTA(VARPTR(CDATA(1)))

          FORTRAN          
          -------

          INTEGER*2 CDATA(66)
          INTEGER*2 STATUS
          INTEGER*2 CLKSTA

          STATUS = CLKSTA(CDATA)


          þ  Description

          clksta  returns  all  of the  information  about  CLOCK.SYS  in a
          structure.  In FORTRAN and  BASIC the structure appears to  be an
          integer array.  The above structure declarations can be  approxi-
          mated  in Pascal.  For  a description of the  values of each ele-
          ment, see the individual APIs below.  The elements  not described
          as part of the input to other functions are:

          unsigned char vers[6];        /* CLOCK.SYS version nnn.nn */
          int clock_type;               /* Type of clock installed  */







                                          42












          CLOCK Version 3.31                               February 4, 1993


          int ct_1;                       /* Data for clock type */
          int ct_2;                                                    
          int ct_3;
          int ct_4;
          unsigned int clock_seg;         /* Segment  CLOCK.SYS loaded at */
          unsigned int clock_long;        /* Size of CLOCK.SYS  */

          CDATA(57) -
          CDATA(59)      =    CLOCK.SYS version LJSF characters
          CDATA(60)      =    Clock type (see type numbers in appendix B)
          CDATA(61)      =    I/O  address,  base memory  segment,  
                              or base year
          CDATA(62)      =    Read memory offset
          CDATA(63)      =    Write-0 memory offset
          CDATA(64)      =    Write-1 memory offset
          CDATA(65)      =    Segment address at which CLOCK.SYS is loaded
          CDATA(66)      =    Length in bytes of CLOCK.SYS


               vers or CDATA(57) - CDATA(59)
                    Is the  version number  of  the CLOCK.SYS  that is  in-
                    stalled.    This is  returned as  a  6-character, left-
                    justified, space-filled  (LJSF) character string.   For
                    example, "3.49  ".


               clock_type or CDATA(60)
                    Is the type number of the clock being used.  See Appen-
                    dix B for the type numbers.

               ct_1 or CDATA(61)
                    Is the value of the first clock parameter.  This is the
                    base  I/O address for  I/O bus clocks,  the base memory
                    segment address for  memory-mapped clocks, or  the base
                    year for the AT&T clocks.

               ct_2 or CDATA(62)
                    Is the read offset for memory-mapped clocks.












                                          43












          CLOCK Version 3.31                               February 4, 1993


               ct_3 or CDATA(63)
                    Is the write 0-bits offset for memory-mapped clocks.


               ct_4 or CDATA(64)
                    Is the write 1-bits offset for memory-mapped clocks.

               clock_seg or CDATA(65)
                    Is the  segment address at  which CLOCK.SYS is  loaded.
                    CLOCK.SYS always starts at offset zero in this segment.


               clock_long or CDATA(66)
                    Is the length of CLOCK.SYS in bytes.

          þ Arguments         cdata
                                   is  a pointer to a location to place the
                                   current    state     information    from
                                   CLOCK.SYS.

          þ  Return Value

          If clksta is  successful, the function returns 0.   Otherwise, it
          returns a non-zero  value and _doserrno is set to the correspond-
          ing error code.  Possible values are:

               0001h     Invalid  function.    This  should  indicate  that
                         CLOCK.SYS is not installed.  It  is the error that
                         the DOS clock device driver  would return since it
                         doesn't handle these functions.

               0005h     Access denied.  Indicates that DOS would not  open
                         a handle for read access.  You may not have enough
                         handles available.


               0006h     Invalid handle.  Should not happen.

               000Dh     Invalid data.  CLOCK.SYS reported a bad byte count
                         or otherwise  did not process  the request.   This
                         should not happen.









                                          44












          CLOCK Version 3.31                               February 4, 1993


          5.3  setpw

          þ Summary

          C          
          -

          #include <ioctl.h>

          extern void pascal far setpw(unsigned char *pw);


          BASIC          
          -----

          DECLARE SUB SETPW(BYVAL S AS INTEGER)

          A$ = "MyPasswd"

          CALL SETPW(SADD(A$))

          Note that A$  must be at least 8 characters long.  Only the first
          8 characters will be used.

          FORTRAN          
          -------

          CHARACTER*8 PW

          PW = "MyPasswd"
          CALL SETPW(PW)

          þ  Description

          The  setpw function sets  the password  to be used  on subsequent
          calls to any  of the following functions.   These functions auto-
          matically  supply   the  most  recent  password  when  they  call
          CLOCK.SYS.   You need not  ever call setpw  if you are  not using
          password protection.  CLOCK.SYS will  only check the password  if
          password protection is enabled through the stmode function.










                                          45












          CLOCK Version 3.31                               February 4, 1993


          þ Arguments         pw
                                   is  a  pointer to  the  password string.
                                   This string should be exactly 8  charac-
                                   ters long and must be at least 8 charac-
                                   ters long.  The  password should also be
                                   LJSF as every  character is significant.
                                   Case is significant in passwords.

          þ  Example


          #include <ioctl.h>

            main()

            {
                    unsigned char pw[9] = "MyPasswd";


            /* Set password to use on subsequent function calls.  */

                    setpw(pw);

            }



          5.4  connec

          þ  Summary

          C          
          -

          #include <ioctl.h>

          extern int pascal far connec(int *conn);

          BASIC          
          -----

          DECLARE FUNCTION CONNEC%(CONN AS INTEGER)

          STATUS% = CONNEC(CONN)


          FORTRAN          
          -------


                                          46












          CLOCK Version 3.31                               February 4, 1993


          INTEGER*2 CONN, STATUS, CONNEC

          STATUS = CONNEC(CONN)


          þ  Description

          The  connec function provides  a means of  setting the connection
          state of CLOCK.SYS.


          þ  Arguments   conn
                              specifies the  new connection mode.  The val-
                              ues are:
                              0 = disconnected (C=D)
                              1 = connected for writes only (C=W)
                              2 =  connected for writes and  periodic reads
                              (C=R)
                              3 = connected for all operations (C=A)


          þ Return Value


          If the  return value  is zero,  the function  succeeded.   If the
          return value is non-zero, an error  has occurred and _doserrno is
          set to the corresponding error code.  Possible values are:

               0001h     Invalid  function.    This  should  indicate  that
                         CLOCK.SYS is not installed.   It is the error that
                         the DOS clock device driver would  return since it
                         doesn't handle these functions.

               0005h     Access  denied.  Indicates that DOS would not open
                         a handle for read access.  You may not have enough
                         handles available.


               0006h     Invalid handle.  Should not happen.

               000Dh     Invalid data.  CLOCK.SYS reported a bad byte count
                         or otherwise did  not process the  request.   This
                         should not happen.







                                          47












          CLOCK Version 3.31                               February 4, 1993


          þ  Example

          #include <stdio.h>
            #include <ioctl.h>


            main()
            {
                  int conn_write = 1;
                  int status;


            /* Set clock to connected for writes */

                  status = connec(&conn_write);
                  if (status)
                        printf("Error %X in connec\n", status);
            }



          5.5  newpw

          þ  Summary

          C          
          -

          #include <ioctl.h>

          extern int pascal far newpw(unsigned char *pw);


          BASIC          
          -----

          DECLARE FUNCTION NEWPW%(BYVAL S AS INTEGER)

          A$ = "MyPasswd"

          STATUS% = NEWPW(SADD(A$))

          Note that A$ must be at least 8 characters long.   Only the first
          8 characters will be used.





               
                                          48












          CLOCK Version 3.31                               February 4, 1993


          FORTRAN          
          -------

          CHARACTER*8 PW

          INTEGER*2 STATUS, NEWPW

          PW = "MyPasswd"
          STATUS = NEWPW(PW)

          þ  Description

          The  newpw function  sets a  new  password for  CLOCK.SYS.   This
          function is  not sufficient to  enable password protection.   You
          must also  use stmode to turn  on password checking.   BE SURE to
          use newpw before you use stmode to turn on password checking.  If
          you turn on password checking without first setting  the password
          to  something that you  know, you will  never be able  to use the
          CLOCK.SYS functions again until you reboot.

          þ Arguments         pw
                                   is  a  pointer to  the  password string.
                                   This string should be exactly 8  charac-
                                   ters long and must be at least 8 charac-
                                   ters long.  The password  should also be
                                   LJSF as every  character is significant.
                                   Case is significant in passwords.

          þ Return Value


          If the  return value is  zero, the  function succeeded.   If  the
          return value is non-zero, an error has  occurred and _doserrno is
          set to the corresponding error code.  Possible values are:

               0001h     Invalid  function.    This  should  indicate  that
                         CLOCK.SYS is not installed.  It is  the error that
                         the DOS clock device driver  would return since it
                         doesn't handle these functions.

               0005h     Access denied.  Indicates that DOS would not  open
                         a handle for read access.  You may not have enough
                         handles available.







                                          49












          CLOCK Version 3.31                               February 4, 1993


               0006h     Invalid handle.  Should not happen.

               000Dh     Invalid data.  CLOCK.SYS reported a bad byte count
                         or  otherwise did not  process the  request.  This
                         should not happen.


          þ  Example

          #include <stdio.h>

            #include <ioctl.h>

            main()

            {
                    unsigned char pw[9] = "MyPasswd";

                    int status;

            /* Set new password for CLOCK.SYS  */

                    status = setpw(pw);
                    if (status)

                        printf("Error %X in setpw\n", status);

            }



          5.6  rstrct

          þ  Summary

          C          
          -

          #include <ioctl.h>

          extern int pascal far rstrct(int *bhour, int *bmin, int *bsec,
              int *fhour, int *fmin, int *fsec);








                                          50












          CLOCK Version 3.31                               February 4, 1993


          BASIC          
          -----

          DECLARE  FUNCTION RSTRCT%(BHOUR%,  BMIN%,  BSEC%, FHOUR%,  FMIN%,
          FSEC%)

          FORTRAN          
          -------

          INTEGER*2 BHOUR, BMIN, BSEC, FHOUR, FMIN, FSEC
          INTEGER*2 RSTRCT


          STATUS = RSTRCT(BHOUR, BMIN, BSEC, FHOUR, FMIN, FSEC)

          þ  Description

          The rstrct  function sets backwards  and forwards limits  on time
          changes.   Any  time changes  that  exceed these  limits will  be
          ignored.  For example,  if a backward limit of 2  seconds is set,
          no change that would move the clock backwards more than 2 seconds
          will be processed.  Setting the limits protects you agains keying
          in a  bad time and agains  programs that may  incorrectly set the
          time.  Yet you  can still change the  time within the  prescribed
          limits.  For example, you  may set a backward limit of  2 seconds
          to permit CLK to adjust the time by up to 2  seconds while inhib-
          iting any  other backwards changes.  These  limits have no effect
          on changing  between standard and daylight  times as that  is not
          really a change in the "time".


          þ Arguments         bhour:bmin:bsec
                                   is the backward limit  in hours, minutes
                                   and seconds.

                              fhour:fmin:fsec
                                   is the forward limit in hours,  minutes,
                                   and seconds.

          þ Return Value

          If the  return value  is zero,  the function  succeeded.   If the
          return value is non-zero, an  error has occurred and _doserrno is
          set to the corresponding error code.  Possible values are:






                                          51












          CLOCK Version 3.31                               February 4, 1993


               0001h     Invalid  function.    This  should  indicate  that
                         CLOCK.SYS is not  installed.  It is the error that
                         the DOS clock device driver  would return since it
                         doesn't handle these functions.

               0005h     Access denied.  Indicates that DOS would not  open
                         a handle for read access.  You may not have enough
                         handles available.


               0006h     Invalid handle.  Should not happen.

               000Dh     Invalid data.  CLOCK.SYS reported a bad byte count
                         or otherwise  did not process  the request.   This
                         should not happen.



          þ  Example

          #include <stdio.h>
          #include <ioctl.h>

          main()
 
          {
              int bhour = 0;
              int bmin = 0;
              int bsec = 2;
              int fhour = 1;
              int fmin = 0;
              int fsec = 0;
              int status;

           /* Set time change limits to 2 seconds backwards and 1 hour 
              forwards */


              status = rstrct(&bhour, &bmin, &bsec, &fhour, &fmin, &fsec);
              if (status)
                   printf("Error %X in rstrct\n", status);
               else
                   printf("Time limits set to -%.2d:%.2d:%.2d,+%.2d:%.2d:%"
                       ".2d\n", bhour, bmin, bsec, fhour, fmin, fsec);

          }




                                          52












          CLOCK Version 3.31                               February 4, 1993



          5.7  stmode


          þ  Summary

          C          
          -

          #include <ioctl.h>

          extern int pascal far stmode(struct modes *mode);

          BASIC          
          -----

          DECLARE FUNCTION STMODE%(MODES%)


          FORTRAN          
          -------

          INTEGER*2 MODES
          INTEGER*2 STMODE

          STATUS = STMODE(MODES)


          þ  Description

          The stmode  function  sets a  variety of  operating  modes.   The
          argument is  actually a  structure of bits.   Each  bit specifies
          whether an operating mode is on (1) or off (0).


          þ Arguments         modes
                                   is  set of  bits that  specify operating
                                   modes.  The bit values are:     

                                   unsigned : 9;            Unused
                                   unsigned day_light: 1;   0x0200 (512)
                                   unsigned disp_24 : 1;    0x0400 (1024)
                                   unsigned disp_tim : 1;   0x0800 (2048)
                                   unsigned pw_ena : 1;     0x1000 (4096)
                                   unsigned disabl : 1;     0x2000 (8192)
                                   unsigned chk_forw : 1;   0x4000 (16384)
                                   unsigned chk_back : 1;   0x8000 (32768)

          

                                          53












          CLOCK Version 3.31                               February 4, 1993


          þ Return Value


          If the  return value  is zero,  the function  succeeded.   If the
          return value is non-zero, an  error has occurred and _doserrno is
          set to the corresponding error code.  Possible values are:

               0001h     Invalid  function.    This  should  indicate  that
                         CLOCK.SYS is not installed.   It is the error that
                         the DOS clock device driver  would return since it
                         doesn't handle these functions.

               0005h     Access denied.  Indicates that DOS would not  open
                         a handle for read access.  You may not have enough
                         handles available.

               0006h     Invalid handle.  Should not happen.

               000Dh     Invalid data.  CLOCK.SYS reported a bad byte count
                         or otherwise  did not process  the request.   This
                         should not happen.


          þ  Example

          #include <ioctl.h>


            main()

            {
                  struct CLOCK_DATA cdata;

            /* Set daylight savings time.  */


                  clksta(&cdata);            /* Get current mode settings. */

                  cdata.mode.day_light = 1;/* Turn on daylight */

                  stmode(&cdata.modes);

            }







                                          54












          CLOCK Version 3.31                               February 4, 1993



          5.8  stzone


          þ  Summary

          C          
          -

          #include <ioctl.h>

          extern int pascal far stzone(int *shour, int *smin, int *ssec,
              unsigned char sname[32], int *dhour, int *dmin,
              int *dsec, unsigned char dname[32]);


          BASIC          
          -----


          DECLARE  FUNCTION  STZONE%(SHOUR%,  SMIN%,  SSEC%,  BYVAL  SN  AS
          INTEGER, DHOUR%, DMIN%, DSEC%, BYVAL DN AS INTEGER)

          SNAME$ = "32-CHARACTER STANDARD ZONE NAME "
          DNAME$ = "Daylight savings time zone name "


          STATUS% = STZONE(6,0,0,SADD(SNAME$),5,0,0,SADD(DNAME$))

          FORTRAN          
          -------

          CHARACTER*32 SNAME, DNAME
          INTEGER*2 STZONE, STATUS

          SNAME = "CST"
          DNAME = "CDT"
          STATUS = STZONE(6, 0, 0, SNAME, 5, 0, 0, DNAME)


          þ  Description

          The stzone function  sets the standard time  and daylight savings
          time offsets  from the calendar  clock and the  standard and day-
          light time  zone names or mnemonics.   Note that the  offsets are
          subtracted from the calendar  clock to get the local time.   Thus
          the standard time offset from UTC to EST is 5:0:0.



                                          55












          CLOCK Version 3.31                               February 4, 1993


          þ Arguments         SHOUR:SMIN:SSEC
                                   is  the time difference between the cal-
                                   endar clock and local standard time.  It
                                   may be a positive of negative value.  If
                                   negative, all three values must be nega-
                                   tive.

                              SNAME
                                   is the standard  time zone name or  mne-
                                   monic.   It must be  a 32-character LJSF
                                   character  string.   As  with  all other
                                   character  strings used  by  these func-
                                   tions,  there  is  no  terminating  NULL
                                   character as  is usual in C.   The other
                                   languages  do  not  readily  handle NULL
                                   terminated strings.   In  C applications
                                   you may  define the  character array  to
                                   contain  33  characters,  but  you  must
                                   ensure that the  NULL character does not
                                   occur in the first 32 characters.


                              DHOUR:DMIN:DSEC
                                   is the time difference  between the cal-
                                   endar clock  and local  daylight savings
                                   time.   Whether  the standard  offset or
                                   the daylight offset is currently used by
                                   CLOCK.SYS is  controlled by the  setting
                                   of the day_light mode bit (see stmode).

                              DNAME
                                   is the  daylight savings time  zone name
                                   or mnemonic.   It must be a 32-character
                                   LJSF character string.


          þ Return Value

          If  the return  value is  zero, the  function succeeded.   If the
          return  value is non-zero, an error has occurred and _doserrno is
          set to the corresponding error code.  Possible values are:









                                          56












          CLOCK Version 3.31                               February 4, 1993


               0001h     Invalid  function.    This  should  indicate  that
                         CLOCK.SYS is not  installed.  It is the error that
                         the DOS clock device driver  would return since it
                         doesn't handle these functions.

               0005h     Access denied.  Indicates that DOS would not  open
                         a handle for read access.  You may not have enough
                         handles available.


               0006h     Invalid handle.  Should not happen.

               000Dh     Invalid data.  CLOCK.SYS reported a bad byte count
                         or otherwise  did not process  the request.   This
                         should not happen.



































                                          57












          CLOCK Version 3.31                               February 4, 1993


          þ  Example

          #include <stdio.h>
            #include <ioctl.h>


            main()

            {
                  unsigned char sname[33] = "PST                             ";
                  unsigned char dname[33] = "PDT                             ";

                  int shour = 8;
                  int smin = 0;
                  int ssec = 0;
                  int dhour = 7;
                  int dmin = 0;
                  int dsec = 0;

                  struct CLOCK_DATA cdata;

            /* Get current status.                                    */

                  clksta(&cdata);


            /* Set time zone to U.S. Pacific time.  */

                  stzone(&shour,&smin, &ssec,sname,&dhour, &dmin,&dsec,dname);

            /* Select daylight savings time.  */


                  cdata.mode.day_light = 1;
                  stmode(&cdata.mode);
            }














                                          58












          CLOCK Version 3.31                               February 4, 1993


          5.9  tdisp

          þ  Summary


          C          
          -

          #include <ioctl.h>

          extern int pascal far tdisp(int *dispx, int *dispy, int *attr);


          BASIC          
          -----

          DECLARE FUNCTION TDISP%(DISPX%, DISPY%, ATTR%)

          STATUS% = TDISP(72, 0, &H79)


          FORTRAN          
          -------

          INTEGER*2 TDISP, STATUS

          STATUS = TDISP(0, 72, 0x79)


          þ  Description

          The  tdisp function sets  the coordinates  and attribute  for the
          continuous  time display.    tdisp  does not  start  or stop  the
          continuous  display nor does it set  the 12-hour or 24-hour mode.
          Those are all provided by the stmode function.

          þ Arguments         DISPX
                                   is the x  (horizontal) cursor coordinate
                                   for  the continuous  time display.   The
                                   rightmost character on a line is at x=0.
                                   Be sure to leave enough space at the end
                                   of the line to accommodate the entire 8-
                                   chararacter time display.   For example,
                                   x=72 is the last position  to specify on
                                   an 80-character line.

                                                                           



                                          59












          CLOCK Version 3.31                               February 4, 1993


                              DISPY
                                   is  the y  (vertical)  cursor coordinate
                                   for the  continuous time  display.   The
                                   top line on the display is y=0.

                              ATTR
                                   is  the display attribute to use for the
                                   continuous time display.  ATTR is usual-
                                   ly  expressed  as two  hex digits.   The
                                   first (high-order)  digit  is the  back-
                                   ground  color (0  to 7)  and  the second
                                   digit is the text or foreground color (0
                                   to  F).  For  example, 0A  would display
                                   bright  green letters  on a  black back-
                                   ground.   Background  colors usually  do
                                   not  include  the  bright  colors.   The
                                   color numbers are:

                                        0    Black
                                        1    Blue
                                        2    Green                         
                                        3    Cyan
                                        4    Red
                                        5    Magenta
                                        6    Brown
                                        7    White
                                        8    Grey                          
                                        9    Bright blue
                                        A    Bright green
                                        B    Brigth cyan
                                        C    Bright red
                                        D    Bright magenta
                                        E    Yellow                        
                                        F    Bright White

          þ Return Value

          If the  return value  is zero,  the function  succeeded.   If the
          return value is non-zero, an  error has occurred and _doserrno is
          set to the corresponding error code.  Possible values are:

                                                                            








                                          60












          CLOCK Version 3.31                               February 4, 1993


               0001h     Invalid  function.    This  should  indicate  that
                         CLOCK.SYS is not  installed.  It is the error that
                         the DOS clock device driver  would return since it
                         doesn't handle these functions.

               0005h     Access denied.  Indicates that DOS would not  open
                         a handle for read access.  You may not have enough
                         handles available.


               0006h     Invalid handle.  Should not happen.

               000Dh     Invalid data.  CLOCK.SYS reported a bad byte count
                         or otherwise  did not process  the request.   This
                         should not happen.



































                                          61












          CLOCK Version 3.31                               February 4, 1993


          þ  Example

          #include <stdio.h>
            #include <ioctl.h>


            main()

            {
                  struct CLOCK_DATA cdata;
                  int dispx = 72;                                          
                  int dispy = 0;
                  int attr = 0x79;

            /* Get current CLOCK.SYS modes.  */

                  clksta(&cdata);


            /* Turn on 12-hour display at end of top line of screen. 
               Use bright blue text on a white backgroun.  */

                  tdisp(&dispx, &dispy, &attr);
                  cdata.mode.disp_tim = 1;                                 
                  cdata.mode.disp_24 = 0;
                  stmode(&cdata.mode);

            }






















                                          62












          CLOCK Version 3.31                               February 4, 1993


          6  CLOCK.SYS - ASSEMBLY LANGUAGE API

          CLOCK.SYS has a  couple of additional APIs  (Application Program-
          ming Interfaces) that  are not present  in the normal  DOS CLOCK$
          device driver.   These interfaces are  provided by the  DOS IOCTL
          (Input/Output  of ConTroL  data) functions.   The  Output Control
          Data to  Character Device function  is used to  set new operating
          values for CLOCK.SYS  for the C=, D=, R=,  TZ=, and /P functions.
          The Input Control Data from  Character Device function is used to
          get the current status  and the date and  time from the  calendar
          clock.


          6.1  Opening the CLOCK$ Device


          In order  to use  the additional APIs  provided by  CLOCK.SYS you
          must  open a handle  to the  CLOCK$ device driver.   You  do this
          using  the DOS  INT  21H Open  File  with Handle  (3DH)  function
          specifying read-write access.  You  then use the handle to invoke
          the other functions.  Sample assembly language is:

               MOV  AX,3D00H            ; Open with read and write access  
               MOV  DX,OFFSET filename  ; Pointer to "CLOCK$" ASCIIZ string
                                        ; DS:DX must point to the string
               INT  21H                 ; Call DOS function handler
          ;    AX contains the handle on return if carry flag is not set.



          6.2  Sending New Values to CLOCK.SYS

          To change the  state of CLOCK.SYS, you use  the Send Control Data
          to  Character Device  (4403H) DOS  function.   You  send data  to
          specify the connection type, modes, time zone offsets and  names,
          restrictions, continuous display information,  and password.  You
          may send  any combination of these in any order.  You must always
          send  the current  password as the  first 8  bytes.   If password
          checking  is not  enabled, it  doesn't  matter what  the 8  bytes
          contain, but you must still send the 8 bytes.

          The  data stream  that  you  send to  CLOCK.SYS  consists of  the
          current password followed by a selection index, the data for that
          selection, another selection index, its data, and so on.






                                          63












          CLOCK Version 3.31                               February 4, 1993


          The selection  indices and the  data stream associated  with each
          one are:

          INDEX     DATA ITEMS     COMMENTS          
          -----     ----------     --------

          1         connected      two  byte   integer  (0 : C=D,  1 : C=W,
                                   2 : C=R, 3 : C=A)

          2         mode           two byte integer  (see stmode for a  de-
                                   scription of the bits)

          3         standard       time_zone structure for standard time
                    daylight       time_zone structure for daylight time

          4         rules          limits structure


          5         display        disp structure

          6         password       8 bytes LJSF of new password





























                                          64












          CLOCK Version 3.31                               February 4, 1993


          Sample assembly language to send new information to CLOCK.SYS:

          curpw     DB   8 dup(?)       ; Current password                 
                    DW   1              ; Change connection
                    DW   2              ;  to C=R
                    DW   4              ; Change limits
                    DW   0,0,2,1,0,0    ;  to R=B-::2,F+1
                    DW   6              ; Set new password
                    DB   "MyPasswd"     ;  to MyPasswd (case is important) 
                    DW   2              ; Change modes
                    DW   0D000H         ;  to enable limits and password
                                        ;  also sets standard time and 
                                        ;  no display
          count     equ $-curpw         ; Length to send
                    ...
                    MOV  AX,4403H       ; Send control data function
                    MOV  BX,handle      ; Value returned from open
                    MOV  CX,count       ; Value = number of bytes to send
                    MOV  DX,OFFSET curpw ; Location of bytes to be sent
                                        ; DS:DX must point to the buffer
                    INT  21H            ;

          ; OK if carry not set.  CX will equal bytes actually taken.


          6.3  Getting Current Status of CLOCK.SYS

          To get the  current status and time, you use  the Receive Control
          Data from Character Device (4402H) function.  You can read all of
          the CLOCK_DATA  structure or  any smaller amount  of it  that you
          need, but you can only read starting at the beginning

          Sample assembly language for reading the clock status is:        

               MOV  AX,440CH            ; Read control data function
               MOV  BX,handle           ; Value returned from open
               MOV  CX,count            ; Number of bytes to read
               MOV  DX,OFFSET buffer    ; Location to store the data
                                        ; DS:DX must point to the buffer
               INT  21H                 ; Call DOS

          ; Data returned if carry not set.
          ; CX will contain the actual number of bytes transferred.







                                          65












          CLOCK Version 3.31                               February 4, 1993


          APPENDIX A:  DEFINITION OF SHAREWARE

          Shareware  distribution  gives  users a  chance  to  try software
          before  buying it.  If you try  a Shareware  program and continue
          using  it, you  are  expected  to register.  Individual  programs
          differ  on  details --  some  request  registration while  others
          require it, some specify a maximum trial period.   With registra-
          tion,  you get anything from  the simple right  to continue using
          the software to an updated program with printed manual.


          Copyright laws apply  to both Shareware and  commercial software,
          and the copyright  holder retains all rights, with a few specific
          exceptions  as stated below.  Shareware authors  are accomplished
          programmers, just  like commercial authors, and  the programs are
          of comparable  quality. (In both  cases, there are  good programs
          and bad ones!) The main difference  is in the method of distribu-
          tion.  The  author  specifically grants  the  right  to copy  and
          distribute the software, either to all and sundry or to a specif-
          ic group. For  example, some  authors require written  permission
          before a commercial disk vendor may copy their Shareware.


          Shareware  is a distribution method, not  a type of software. You
          should  find software  that  suits  your  needs  and  pocketbook,
          whether it's  commercial or Shareware. The Shareware system makes
          fitting your  needs easier, because you  can try before  you buy.
          And because the  overhead is low, prices are  low also. Shareware
          has the  ultimate money-back guarantee  -- if  you don't use  the
          product, you don't pay for it.

          DISCLAIMER - AGREEMENT

          Users  of CLOCK must accept this  disclaimer of warranty:  "CLOCK
          is supplied  as is.   The  author disclaims  all warranties,  ex-
          pressed or implied, including, without limitation, the warranties
          of merchantability  and of fitness for  any purpose.   The author
          assumes no liability for damages, direct  or consequential, which
          may result from the use of CLOCK."

          CLOCK is a  "shareware program" and is  provided at no charge  to
          the  user for  evaluation.   Feel  free  to  share it  with  your
          friends, but please  do not give  it away altered  or as part  of







                                          66












          CLOCK Version 3.31                               February 4, 1993


          another system.   The essence of "user-supported"  software is to
          provide  personal  computer users  with quality  software without
          high prices,  and yet  to provide  incentive  for programmers  to
          continue to  develop new  products.   If  you find  this  program
          useful and  find that  you are  using CLOCK  and continue  to use
          CLOCK after a reasonable trial  period, you must make a registra-
          tion payment of $10 to Ronald Q. Smith.  The $10 registration fee
          will license  one copy  for use on  any one  computer at any  one
          time.  For a registration fee of $25, I will immediately send you
          the  latest version of  CLOCK including the  source code and this
          document as a WordPerfect 5.1 file.   You may use the source code
          for your own  maintenance of CLOCK or as a  learning tool for any
          software that you develop.   You may not  use all or part  of the
          source code in any software that you develop or release to others
          without the permission of Ronald Q. Smith.


          You must treat  this software just  like a book.   An example  is
          that this software may be used by any number of people and may be
          freely moved  from one computer  location to another, so  long as
          there is  no possibility of it  being used at  one location while
          it's being used at another.  Just as a book cannot be read by two
          different persons at the same time.

          Commercial users of CLOCK must register and pay for  their copies
          of CLOCK  within 30 days of  first use or their  license is with-
          drawn.    Site-License arrangements  may  be  made by  contacting
          Ronald Q. Smith.


          Anyone distributing CLOCK for any kind of remuneration must first
          contact Ronald Q. Smith at the address below for authorization.

          You are encouraged to  pass a copy of CLOCK along to your friends
          for evaluation.  Please encourage them  to register their copy if
          they find  that  they can  use  it.   All registered  users  will
          receive a copy of the latest version of the CLOCK system.

          Send the fees and any inquiries to:

                         Ronald Q. Smith                                   
                         11 Black Oak Road
                         North Oaks, MN 55127-6204







                                          67












          CLOCK Version 3.31                               February 4, 1993


          You may also contact me via CompuServe mail at userid  71620,514.
          I will be  happy to respond  to any problems and  suggestions for
          future capabilities.


          You may register CLOCK through the CompuServe Shareware Registra-
          tion program.  CLOCK.SYS is found under registration ID 104.  The
          fee  for registering through  CompuServe is  $12 (to  cover their
          charge) and will be added directly to your CompuServe bill.









































                                          68












          CLOCK Version 3.31                               February 4, 1993


          APPENDIX B:  CLOCK TYPES                                         


          B.1  Type 0 - PC/AT

          IBM PC/AT and  all fully compatible  PCs.   Most versions of  DOS
          fully support  this clock  interface without  a separate  driver.
          Use CLOCK.SYS to provide support for CLK.EXE and CLKDEMO.EXE.  If
          you don't  need the  extra functions of  CLK, you  probably don't
          need CLOCK.SYS.  However,  there were a couple  of late 8088  PCs
          that adopted  the PC/AT  clock standard but  did not  provide the
          PC/AT recognition  sentinel.  DOS  will not  find the clock,  but
          CLOCK.SYS will.

          Amstrad PC1521DD systems use this type of clock.

                          
          Automatic  determination checks  location  F000:FFFE for  the hex
          value FC.

          BIOS calls are used  to read and write the clock values which are
          usually  stored in  the CMOS  RAM along with  other configuration
          information.  The primary interfaces are:
                          
               Get Date: MOV  AH,4
                         INT  1AH
                              Returns the year in  CX and month and  day in
                              DX in BCD  format (e.g., a hex  display would
                              show:  CX=1991, DX=1009 for October 9, 1991).

               Set Date: MOV  AH,5
                              Load CX and DX as above for Get Date
                         INT  1AH


               Get Time: MOV  AH,2
                         INT  1AH
                              Returns hours  and minutes in CX  and seconds
                              in DH in BCD format.   May also return 100ths
                              of seconds in DL (e.g., CX=2359, DX=5900  for
                              1 second before midnight).









                                          69












          CLOCK Version 3.31                               February 4, 1993


               Set Time: MOV  AH,3
                              Load CX and DX as for Get Time
                         INT  1AH




          B.2  Type 1 - Zenith Z-18x portables, Supersport 20

          Automatic determination checks  location F000:FFFA  for the  two-
          byte hex value 4D32 ("M2").

          BIOS calls are used to read and write the clock.

               Get Date: MOV  AH,2
                         INT  1AH                                          
                              Returns CX=year (1980  - 2079) in binary  and
                              DH=month, DL=day.  All  values are binary.  A
                              hex display of the above date would look like
                              CX=7C7, DX=A09.

               Set Date: MOV  AH,3                                         
                              Load CX and DX as for Get Date.
                         INT  1AH

               Get Time: MOV  AH,4
                         INT  1AH
                              Returns  CH=hours, CL=minutes, DH=seconds.  A
                              hex display would show: CX=173B, DX=3B00.

               Set Time: MOV  AH,5
                              Load CX and DX as for Get Time.
                         INT  1AH



          B.3  Type 2 - Various Zenith Data System PCs.

          Automatic  determination  looks  at  location F000:800A  for  the
          pattern 00,F0,"ZDS".










                                          70












          CLOCK Version 3.31                               February 4, 1993


               Get Date: MOV  AH,2AH
                         INT  1AH
                              Returns CX and DX as for type 1.


               Set Date: MOV  AH,2BH
                              Load CX and DX as for type 1.
                         INT  1AH

               Get Time: MOV  AH,2CH                                       
                         INT  1AH
                              Returns CX and DX as for type 1.

               Set Time: MOV  AH,2DH
                              Load CX and DX as for type 1.
                         INT  1AH



          B.4  Type 3 - Memory-Mapped Clocks

          Memory-mapped  clock used  on some  Zenith Data  Systems  PCs and
          other similar clocks including many slot-less or  no-slot clocks.
          The  SMT (Systems  Manufacturing Technology)  No-Slot clocks  are
          supported by this type.

          Automatic determination  is to  attempt to  read the  clock.   If
          values other than all 0FFH or 0 are obtained, this  clock type is
          chosen.  All known segments and offsets are tried.


          Several different  memory mapping  approaches are  used and  many
          different address  possibilities are  supported.   In  general  a
          segment address in the ROM region (C800H through FFFFH) is  used.
          Offsets from that  segment address are used  to read bits,  write
          zero bits, and write  one bits.  Documentation may  specify those
          segments  and addresses in  several forms.   For example, segment
          F000 with offset F002 is the same as segment FF00 with offset 2.

          Each memory reference  reads or writes a single bit.  Read opera-
          tions  are  used for  all  references with  separate  offsets for
          reading a bit, writing a zero bit, and writing a one bit.


          Clock segments and addresses currently probed include:





                                          71












          CLOCK Version 3.31                               February 4, 1993



            SEGMENT   WRITE0   WRITE1   READ    DECR     LAST     VENDOR


             F000       F002     F003    F004    0000    F000    (Zenith)

             FE00       2        3       5       0080    C800    SMT

             FE00       0        2       8       0080    C800    SMT

          Multiple  address combinations may  be tried for  each clock pat-
          tern.   The DECR  value is subtracted from  the SEGMENT value for
          another attempt  at probing until  the value  equals LAST.   Note
          that  like the  SEGMENT address,  DECR and LAST  are in  units of
          paragraphs (16-bytes).   Thus DECR of 80 is equivalent to 800H or
          2048 bytes.

          When  the addresses used by  a memory-mapped clock are determined
          by probing, the segment  and read address  is displayed.  As  the
          read address  varies  the most  from  one clock  manufacturer  to
          another it is a good indication of the type of clock found.

          Data is stored in BCD in bytes that you construct by  shifting in
          the bits.  The most important data bytes are: 

               0 = Hundredths of seconds
               1 = Seconds
               2 = Minutes
               3 = hours
               5 = days
               6 = months
               7 = years mod 1980



          B.5  Type 4 - Direct Register I/O Bus Clock

          Many  add-in clocks on  expansion boards use  this type of clock.
          Some built-in clocks in  PCs are also  accessed similarly.   This
          clock was  used on many AST Research I/O boards for 8088 PCs such
          as the Six-Pack  Plus, IO  Plus, etc.   Also used  on some  Tandy
          systems (e.g., 1200HD) and the Vendex Turbo-888-XT.








                                          72












          CLOCK Version 3.31                               February 4, 1993


          Automatic determination is to attempt to read, complement, write,
          re-read, and re-complement  one of the registers.   If the  first
          value read  and the re-complemented  second value are  equal, the
          register exists and is presumed to be the clock.

          See also the description for  types 6 and 7.  If you  aren't sure
          which variant you have, specify type 8 and automatic probing will
          determine if it is  really a type 4, 6,  or 7.  For  the greatest
          chance of detecting  the correct clock type, supply  the base I/O
          address if at all possible.

          NOTE:  If the clock is not correctly  initialized (e.g., you have
          just  replaced the battery), CLOCK.SYS must initialize it so that
          the counters  will start working.  CLOCK.SYS  determines that the
          clock has been previously initialized by looking at  register 14H
          (see B below).  If register B contains  the value 0DEH, the clock
          is presumed to be initialized.  If  not, CLOCK.SYS will clear all
          the registers to zero and start the counters running.  While this
          form  of  checking  for initialization  was  commonly  used, your
          previous software may have used  a different method.  If  so, the
          first time  you run CLOCK.SYS  your date and  time may be  set to
          zero  (1980-1-1 00:00:00).  If that  happens, just enter the date
          and time.  It should work OK after that without resetting to zero
          on further boots.

          Each clock register is implemented as a separate I/O register ad-
          dress.   Clock base I/O addresses  of 240H, 2C0H, 300H,  and 340H
          are supported by automatic probing.  Similar clocks at other base
          I/O addresses  are supported  by specifying type  4 and  the base
          address. The address range  used is the  base plus 0 through  1FH
          (e.g., 2C0H through 2DFH).
                          


















                                          73












          CLOCK Version 3.31                               February 4, 1993


          Important registers are (using 2C0 as the example):
                          
               2C1  =  100ths of seconds                                   
               2C2  =  seconds 
               2C3  =  minutes 
               2C4  =  hours 
               2C6  =  days
               2C7  =  months
               2C9  =  month last time clock was read/set                  
               2CA  =  years
               2CB  =  initialized flag (0DEH if initialized)
               2D4  =  Status
                              
          All values are in BCD.  That means that each register consists of
          two 4-bit nybbles (a nybble is to a nibble as a byte is to a bite
          - I haven't seen this  used recently, but as a bit of trivia, the
          first IBM 360 principles of operation manuals used  that term and
          that spelling -  at least in a  draft copy that we got  in 1965).
          Each nybble contains  one decimal digit of the  value.  Years are
          mod 1980 (i.e., 0 means 1980, 99 means 2079).


          Since these  clocks do not keep  the year and do  not handle leap
          years for you, CLOCK.SYS does the necessary calculations to  keep
          the  year correctly  maintained and to  adjust the  date for leap
          days.   The  clocks do  provide a couple  of memory  locations in
          which CLOCK.SYS maintains  the year and previous month.   As long
          as you boot your system before  a full year has passed, CLOCK.SYS
          will correctly maintain the date.


          B.6  Type 5 - Mitsubishi 8088 PCs

          These were sold by Sperry as the PC-1 and  PC/HT, by Leading Edge
          as the Model D, by Mitsubishi, and others.

          Automatic determination checks location  F000:FFB3 for the string
          "MITSUBISHI".  Later Mitsubishi PCs  which used a different clock
          had  the same string at a different  location.  We hope all early
          versions had it at this location.










                                          74












          CLOCK Version 3.31                               February 4, 1993


          BIOS functions are used to access the clock.

               Get Date: MOV  AH,4                                         
                         INT  1AH
                              Returns  CL=year  mod  1980,  DH=month,   and
                              DL=day all  in binary.  Also  sets AL=0FFH if
                              the clock is  busy and the request  should be
                              retried.


               Set Date: MOV  AH,5
                              Load CL, DX as for Get Date.
                         INT  1AH
                              Returns AL=0FFH if busy.

               Get Time: MOV  AH,2                                         
                         INT  1AH
                              Returns  CH=hour,  CL=minute, DH=second,  and
                              AL=status.  AL=0FFH means  busy.  AL=0  means
                              24-hour mode.   AL=1 means AM and  AL=3 means
                              PM.


               Set Time: MOV  AH,3
                              Load AL, CX, DH as for Get Time.
                         INT  1AH
                              Returns AL=0FFH if busy.

          NOTE:  Some early Mitsubishi PCs came with fixed disk controllers
          that were not DOS compatible.  In addition to the clock modifica-
          tions, the DOS for those systems also handled the disk controller
          variant.  If  you have such a PC, CLOCK.SYS  is not sufficient to
          enable you to  go above DOS  level 3.2.   You will  also need  to
          replace your fixed  disk controller.  I strongly suggest that you
          create a boot floppy for your current DOS level before you try to
          install your new DOS level.  Then boot your new DOS from a floppy
          disk, do SYS C: and copy COMMAND.COM to C:, then try a disk boot.
          If the disk boot fails, boot the floppy you just created and do a
          SYS C:  and copy COMMAND.COM to  C: to restore your  old DOS ver-
          sion.  At that point, your best bet is to simply give up and stay
          with DOS 3.2. If you want to proceed, you must replace your fixed
          disk controller.








                                          75












          CLOCK Version 3.31                               February 4, 1993


          If  SYS C: gives  you an error  status that  indicates that there
          isn't room  for the new  DOS version  (very possible when  moving
          from 3.2 to 3.3 or above), you must backup your entire fixed disk
          and use FORMAT C:/S  to place the new version of DOS on the disk.
          While this is a hassle, at  least if your PC won't boot from  the
          disk, the fall-back approach is identical.  There will be room to
          put DOS 3.2 or earlier back on the fixed disk.



          B.7  Type 6 - Indirect Register I/O Bus Clock

          Used on AST Research boards and others.   Typically uses the same
          I/O  base address  as type 4.   However  the clock  registers are
          selected by sending the register address to the base  I/O address
          and then  reading or writing  data at the  base I/O address  + 1.
          The internal register numbers and  their contents are the same as
          for type 4.

          Automatic determination by probing the  address register.  If the
          low-order bit is one, it may be this type of clock or type 7.  We
          then look further to  determine if it is type  7.  If you  aren't
          sure which type of clock you have but believe it is type 4,  6 or
          7, specify type 8 and automatic probing will detect which variant
          it is.  If at all possible  specify the base I/O address as  that
          will increase  the likelihood  that the correct  determination is
          made.


          I/O  addresses  used are  (again using  2C0  as the  example base
          address):

               2C0    =  Address register.  Writing a value to this address
                         selects the internal register to read or write.
               2C1    =  Data register.   Reading or writing  this address,
                         reads  or writes the  internal register previously
                         selected by writing 2C0.













                                          76












          CLOCK Version 3.31                               February 4, 1993


          The internal register numbers are (the values to write to 2C0):

                1  =  100ths of seconds                                    
                2  =  seconds
                3  =  minutes
                4  =  hours
                6  =  days
                7  =  months
                9  =  month last time date was read or written             
                A  =  year
                B  =  initialization flag
               14  =  status
                          
          Other processing is the same as type 4.



          B.8  Type 7 - Complex I/O Bus Clock

          Used on AST Research boards and others.  Typically uses the  same
          base I/O address as types  4 and 6.   Type 7 uses a more  complex
          register access sequence than type 6.  Type 7  can be detected by
          looking to see if the value in register D has bit 1 (value=2) set
          which type  6 will not.  If  you aren't sure which  type of clock
          you have  but believe it  is type 4, 6  or 7, specify  type 8 and
          automatic probing  will detect which  variant it is.   If at  all
          possible specify the  base I/O address as that  will increase the
          likelihood that the correct determination is made.


          The  base I/O address is used as an address register and the base
          + 1 as a data  register.  This is the  same as for clock type  6.
          However, the internal  registers and the form of  the commands is
          quite  different.   The primary difference  is that  the internal
          registers only hold  four bits of data each.   Thus each internal
          register represents a single decimal digit.














                                          77












          CLOCK Version 3.31                               February 4, 1993


          The I/O addresses are used as follows (using 2C0 as an example):

               2C0     = Address register.  The number  of an internal reg-
                         ister plus 80H  is written to this I/O  address to
                         select an internal register.

               2C1     = Data register.    Four bits  of data  are read  or
                         written  using  this I/O  address from  or  to the
                         internal register  previously selected  by writing
                         to 2C0.

          The internal registers are:

               0  =  Units digit of seconds
               1  =  Tens digit of seconds                                 
               2  =  Units digit of minutes
               3  =  Tens digit of minutes
               4  =  Units digit of hours
               5  =  Tens digit of hours
               6  =  Day of week
               7  =  Units digit of day of month                           
               8  =  Tens digit of day of month
               9  =  Units digit of month
               A  =  Tens digit of month
               B  =  Units digit of year
               C  =  Tens digit of year
               D  =  Function register                                     
               E  =  Function register
               F  =  Function register


          B.9  Type 8 - Generic I/O Bus Clock


          Type unknown.  Probe only for types 4,  6, 7, 9, and B.  Use type
          8 if you are sure that you have an I/O bus clock (i.e., the clock
          is on an add-in card) but aren't sure whether it is type 4, 6, 7,
          9, or B.  If at all possible,  supply the base I/O address of the
          clock as this will greatly increase the likelihood of the correct
          handling method being chosen.










                                          78












          CLOCK Version 3.31                               February 4, 1993


          B.10 Type 9 - Quadram I/O Bus Clock

          This  type  was  used by  Quadram  Corporation  on  the QuadCard,
          QuadCard II, and QuadCard 512+.  It may  have been used on others
          as well.

          Automatic determination checks to see that I/O registers exist at
          310H or 210H.


          This clock  used four I/O  control registers and  twelve internal
          registers.  The I/O registers (using 310H as the example) are:

               310  =  Data register (used to move data values)
               311  =  Address register (used to select internal register)
               312  =  Function register (Read, write, hold counter)       
               313  =  Control register (Enables read or write function)

          The internal registers are:

                0 = Units digit of seconds                                 
                1 = Tens digit of seconds
                2 = Units digit of minutes
                3 = Tens digit of minutes
                4 = Units digit of hours
                5 = Tens  digit of hours - Also uses bit 2 (=4) to indicate
                    PM if in  12-hour mode and bit 3 (=8) to select 24-hour
                    mode
                6 = Day of week (we don't use this)
                7 = Units digit of days
                8 = Tens digit of  days - Also uses bit  3 (=8) to indicate
                    that this  is a  leap year.   This bit  must be  set by
                    software whenever there is less than 366 days until the
                    next leap day.  If you  do not boot within that period,
                    leap day will not be taken.
                9 = Units digit of months
               10 = Tens digit of months
               11 = Units digit of year mod 1980
               12 = Tens digit of year mod 1980


          NOTE:  If you have this type  of clock, you can only set the time
          to the nearest minute.  Whenever the time is set, the seconds are







                                          79












          CLOCK Version 3.31                               February 4, 1993


          always  set to  zero.   You  should set  the time  as the  minute
          changes.  For that reason, you will not want to use the automatic
          adjustment capability of CLK  with this type of clock  as it will
          try to set the time to the nearest second.


          B.11 Type A - AT&T 6300, 6300 PLUS, 6300 WGS

          Automatic probing  is accomplished by  trying to read  the clock.
          If the read attempt  using the BIOS is successful (carry flag not
          set) and the values returned look like a valid time, the clock is
          assumed to be present.

          NOTE:   AT&T clocks do not advance the  year on January 1.  It is
          necessary to  change  the date  at the  beginning  of each  year.

          Also, AT&T clocks always clear the  seconds to zero when the time
          is changed.  For  this reason you should always set  the date and
          time at the beginning of a  minute.  You should also not use  the
          automatic adjustment feature of CLK with these clocks.

          A base year may  be specified on the DEVICE= line.  If it is not,
          1992  will be used.   This base  will be good  for all dates from
          1992-1-1 till 1999-12-31.

          BIOS functions are used with this clock.

               Get Date: MOV  AH,0FEH                                      
                         INT  1AH
                              Returns BX =  Days since base, CH = Hours, CL
                              = Minutes,  DH = Seconds, DL = 100ths of sec-
                              onds

               Set Date: MOV  AH,0FFH                                      
                         MOV  BX,Days since base
                         MOV  CH,Hours
                         MOV  CL,Minutes
                         MOV  DH,0
                         MOV  DL,0
                         INT  1AH










                                          80












          CLOCK Version 3.31                               February 4, 1993


          B.12 Type B - Hyundai 8088 clock

          Automatic determination probes  the control registers.   If they,
          appear to be present, CLOCK tries to read  the clock.  Legal time
          and date values will select this clock.

          This clock uses I/O addresses E0H through EFH as follows:
               E0  =  Units digit of seconds
               E1  =  Tens digit of seconds                                
               E2  =  Units digit of minutes
               E3  =  Tens digit of minutes
               E4  =  Units digit of hours
               E5  =  Tens digit of hours
               E6  =  Day of week
               E7  =  Units digit of days                                  
               E8  =  Tens digit of days
               E9  =  Units digit of month
               EA  =  Tens digit of month
               EB  =  Units digit of year
               EC  =  Tens digit of year
               ED  =  Control                                              
               EE  =  Control
               EF  =  Control



























                                          81












          CLOCK Version 3.31                               February 4, 1993


          APPENDIX C:  REVISION HISTORY

          930204 -  Version 3.31: Fixed bug in CLOCK.SYS with binary clocks.

          930130 -  Version 3.30:  Added  support for  a  password and  for
                    saving  the current  CLOCK.SYS state as  a new  copy of
                    CLOCK.SYS  for future booting.   Added  continuous time
                    display.   Changed  API to  support  direct calls  from
                    BASIC,  FORTRAN,  and Pascal  as  well as  C  and MASM.
                    Changed status display to be easier to read.


          930115 -  Version 3.24: Converted document to WordPerfect 5.1 and
                    rewrote much  of  it.   Provide  document  in  standard
                    release that can either be viewed on-line or printed.

          930110 -  Version 3.23:  Added support  for R=  and W=  commands.
                    Fixed handling of CLK.INI file  so that we don't try to
                    update  it  if it  is read  only or  is in  a read-only
                    sub-directory.   We also  don't update  it if  we can't
                    find  the [clk]  section as  it may  be someone  else's
                    file.


          930106 -  Version  3.22: Fixed bug  in CLK.EXE that  caused it to
                    move the CLK.INI file to the root directory.

          930104 -  Version 3.21: Fixed bug in CLOCK.SYS expecting zero for
                    100ths of seconds from CMOS clock  but some BIOSs don't
                    zero the register.  Fixed  bug in CLK with synchroniza-
                    tion algorithm not correctly waiting for a new second.

          930102 -  Version 3.20:  Add support for a command file, automat-
                    ic adjustment, and improved synchronization.  My thanks
                    to Eric Smith for the ideas that lead to these enhance-
                    ments.


          921230 -  Version 3.11:  Simplified logic in CLOCK.SYS for check-
                    ing if calendar clock should be read.

          921229 -  Version  3.10: Add support for constant synchronization
                    with calendar clock.  Fix bug in calculating dates near
                    the end of leap years.






                                          82












          CLOCK Version 3.31                               February 4, 1993


          921226 -  Version 3.02: Recompile CLK.EXE and CLKDEMO.EXE to only
                    use 8088 instructions.  Version 3.01 inadvertently com-
                    piled with 80286  instructions which  can lock up  8088
                    systems.

          921221 -  Version  3.01: Fixed  a  couple of  bugs  in beta  test
                    version 3.00 with non-PC/AT clocks.  Added logic to CLK
                    to  display  the pre-defined  time zones  on  errors or
                    request.


          921219 -  Version 3.00: Added support for automatic time zone and
                    daylight savings  time adjustment.   CLOCK.SYS  now has
                    the ability to manage  the DOS real time clock  and the
                    battery-protected clock separately.  CLK.EXE is used to
                    convert  a base value in the battery-protected clock to
                    a correct local time in the DOS clock.

          920614 -  Version 2.24: Fixed bug in probing of AT&T 6300 clocks.
                    Some of the  clocks do not set AL  on successful opera-
                    tion.


          920604 -  Version  2.23:  Fixed  bug causing  fall  through  into
                    memory probing when only I/O probing was wanted.

          920411 -  Version 2.22: Changed order of probing to probe memory-
                    mapped clocks  last as they are  being spuriously found
                    on some Tandy systems.


          920401 -  Version  2.21:  Changed pattern  of I/O address probing
                    to probe all possible I/O addresses for one type (e.g.,
                    4) before trying any  for another type.   Try to  avoid
                    finding the wrong type.   Added the type B clock to the
                    type 8 probe.


          920328 -  Version 2.20:  Changed order of I/O address probing for
                    clock  types 4,  6,  and 7  to  avoid, where  possible,
                    accessing  other boards.  Most  commonly used I/O clock
                    addresses, I hope, are now probed first.


          920322 -  Version 2.19:  Improved probing for I/O clocks to check
                    that legal values are found in all the data  registers.




                                          83












          CLOCK Version 3.31                               February 4, 1993


                    Several of  the I/O  clocks use operation  sequences so
                    much like each  other that it is possible to choose the
                    wrong one if we  don't actually read the time  and date
                    and  see if  the values  are legal.   This  approach to
                    probing may possibly result in not finding a clock that
                    is present  but that  has been totally  reset.   Such a
                    clock should  be found  on a  second try  to boot  with
                    CLOCK.SYS as the counters will have advanced by then.


          920320 -  Version  2.18:   Added probing  for generic  PC/AT type
                    clock on systems that don't have the PC/AT signature in
                    the BIOS.

          920307 -  Version 2.17:  Added Hyundai 8088 clock.


          920112 -  Version 2.16:  Added AT&T 6300 clock.

          920111 -  Version 2.15:  Fixed memory address used by one type of
                    SMT No-Slot clock.

          920105 -  Version  2.14:   Added support  for a wider  variety of
                    memory mapped  clocks including the SMT  (Systems Manu-
                    facturing Technology) No-Slot clocks.

          911208 -  Version 2.13:  Add  probing for Vendex Headstart Turbo-
                    888-XT system and any other  I/O clock at 300H.  Change
                    I/O clock probing logic to make it less  likely to find
                    the wrong type by accident.

          911129 -  Version 2.12:  Fix handling of Quadram clocks (type 9).
                    They can only set seconds to zero so generate an  error
                    if anyone tries to set the seconds to any other value.


          911128 -  Version  2.11:    Fix  bug in  handling  clock  type 9,
                    Quadram clocks that left clock  turned off after opera-
                    tions.   Also fix bug  in busy determination  for clock
                    types 4 and  6 that could result in a decision that the
                    clock was not operational.









                                          84












          CLOCK Version 3.31                               February 4, 1993


          911121 -  Version 2.10:  Add clock types 6  ,7 and 9.  Add type 8
                    to do specific  probing for the  various I/O bus  clock
                    types.


          911109 -  Version  2.05:  Fix  bug in  leap day handling  for I/O
                    clocks.  Fix bug that caused hung systems  when setting
                    the date or time on Z-18x portables.

          911026 -  Version 2.04:  Add support  for I/O clocks at addresses
                    240H  and 340H.    Reduce resident  memory required  by
                    clock driver to  only that required for  specific clock
                    type.

          911021 -  Version  2.03:   Change handling of  new day  flag from
                    BIOS to  accommodate BIOSs that indicate  multiple days
                    have passed.

          911020 -  Version  2.02:  Fix bug in returning date on clock read
                    functions.  Added message in automatic determination to
                    indicate type found.


          911010  - Version   2.01:    Added   automatic  determination  of
                    Mitsubishi 8088  PC clocks.  Fixed handler  to keep the
                    BIOS  counter set  properly for  programs that  read it
                    directly.   Also  returns  a  finer  granularity  value
                    (100ths of seconds) on reads.


          911009  - Version 2.00:  Modified  clock driver to support  addi-
                    tional clock types.  Thanks to Eric Smith (no relation)
                    for help in finding out how the Zenith PC clock worked.

          911005  - Version 1.20:  Changed prologue and epilogue to conform
                    to DOS 5.00 documentation.   Seems to work OK  with DOS
                    5.0 without  the changes, but we might  as well be con-
                    sistent to save problems later.

          910903  - Version 1.10:   Added display of current  date and time
                    when initializing.









                                          85












          CLOCK Version 3.31                               February 4, 1993


          910518  - CLOCK version  1.00.  Initial version  developed at the
                    request  of a friend with a  Sperry PC/HT who wanted to
                    move to DOS 4.01.


          1984    - Write clock  device driver for AST clock  for IBM PC-1.
                    This serves as the introduction to what device  drivers
                    and especially the CLOCK$ driver are all about.










































                                          86