K83LOOP - test your Marklin K83 decoders and switchpoints
        ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
                   Copyright 1993   Rob Hamerling

  K83LOOP is a simple program to test if your switchpoint decoders
  (and the switchpoints themselves) are working properly. All switches
  in a specified range are switched forward ('branch-off') and backward
  ('straight') and switched off with a certain wait-time between these
  commands. This wait-time can be specified.
  The COM-ports to which the Marklin Interface is supposed to be connected
  can be specified as well.


  Deliverables:
  ÍÍÍÍÍÍÍÍÍÍÍÍ
  There are 3 versions of K83LOOP, all with the same functionality:

     K83LOOP.EXE   - DOS
     K83LOOP2.EXE  - 16-bits version for OS/2 1.3, 2.0 or higher
     K83LOOP3.EXE  - 32-bits version for OS/2 2.0 or higher


  Command parameters
  ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
  The following parameters can be specified with execution of K83LOOP (all
  variants the same) in the following sequence:

    K83LOOP  'first'  'last'  'port'  'pause'

              first  -  first switch address to be tested
              last   -  last address to be tested (default 256)
              port   -  COM-port number (default 1)
              pause  -  Wait-time in milliseconds between commands
                        (default 250)

  Note that the 'wait-time' is actually the time a switchpoint gets its
  current, until the 'switch-off' command is executed.

  Only the first parameter is required. If you start K83LOOP without
  parameters, you will be reminded of the parameters!

  K83LOOP can be terminated while running with Ctrl-Break.


  Sample report:
  ÍÍÍÍÍÍÍÍÍÍÍÍÍ
  K83LOOP reports its activity on your display. If you call K83LOOP for
  example with:

     K83LOOP  253 4 2 250

  you may see the following report:

  switch     branch   straight  switchoff
  number      time      time      time
  ------     -------   -------   -------
    253        0.000     0.281     0.531
    254        0.781     1.093     1.343
    255        1.593     1.843     2.093
    000        2.343     2.593     2.843    (note: 000 equivalent of 256)
    001        3.093     3.343     3.593
    002        3.843     4.093     4.343
    003        4.593     4.843     5.093
    004        5.343     5.593     5.843

  Notes: - times may be rounded to the next timer-tick value!
         - 'wrapping' of switchpoint addresses takes place when 'first'
           address is higher than 'last'.


  Internals
  ÍÍÍÍÍÍÍÍÍ
  K83 is a simple application which makes use of the MKLAPI, one of my
  other products for programming the Marklin Digital system. MKLAPI is a
  'driver' and high level Application Programming Interface (API).
  See the MKLAPI package on the international FIDO Bulletin Board
  network (in particular the Fernwood OS/2 program collection) for the
  latest version.

  K83LOOP is written in standard C-language. The source code of K83LOOP
  will be available from me, when you register your MKLAPI package!


  Feedback
  ÍÍÍÍÍÍÍÍ
  Comments, suggestions and problem reports are welcome. Send written
  notes to:
               R. Hamerling
               Hogelandseweg 67
               4132 CV  Vianen
               The Netherlands
               phone: 31.3473.72136  (voice)

  Or send a message via the FIDO Bulletin Board network to:

               Rob Hamerling  at  2:512/4.1098