MKLAPI
                                                                             
                                                 M„rklin-Interface driver and
                                                          High Level Language
                                            Application Programming Interface
                                                     for C-language and BASIC
                                                                  Version 1.0
                                                                             



                                                Document Number RH-MKLAPI 1.0

                                                                  May 4, 1993


                                                                Rob Hamerling

                                                                    Vianen-ZH
                                                              The Netherlands
                                                 Phone: 31-3473-72136 (voice)
                                                           FIDO: 2:512/4.1098

                                                                       MKLAPI




  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  CONTENTS


    Introduction  . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 1
    What is MKLAPI?   . . . . . . . . . . . . . . . . . . . . . . . . . . . 1
    Purpose   . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 1
    Realisation   . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 2
    Registration  . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 2

    Functional description  . . . . . . . . . . . . . . . . . . . . . . . . 3
    Overview  . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 3
    Terminology   . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 3
    Functional Requirements   . . . . . . . . . . . . . . . . . . . . . . . 3
    Provided Facilities   . . . . . . . . . . . . . . . . . . . . . . . . . 4
    Deliverables  . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 4
    Prerequisites   . . . . . . . . . . . . . . . . . . . . . . . . . . . . 5
    Restrictions and Limitations  . . . . . . . . . . . . . . . . . . . . . 5
    Tests   . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 6
    C-language framework  . . . . . . . . . . . . . . . . . . . . . . . . . 7
    QuickBASIC framework  . . . . . . . . . . . . . . . . . . . . . . . . . 8
    Sample programs   . . . . . . . . . . . . . . . . . . . . . . . . . . . 8
    OS/2 and DOS differences   . . . . . . . . . . . . . . . . . . . . . . 10

    Specifications   . . . . . . . . . . . . . . . . . . . . . . . . . . . 11
    Available Functions  . . . . . . . . . . . . . . . . . . . . . . . . . 11
    mklclose   . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 11
    mklflush   . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 12
    mklgetsn   . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 13
    mklgo  . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 13
    mklmsecs   . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 14
    mklopen  . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 15
    mklpoll  . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 16
    mklpurge   . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 16
    mklputc  . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 17
    mklsleep   . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 18
    mklsound   . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 18
    mklstats   . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 19
    mklstop  . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 21
    mkltime  . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 22
    mkltrace   . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 22
    Macro Specifications   . . . . . . . . . . . . . . . . . . . . . . . . 23
      mklput1c   . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 23
      mklput2c   . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 24
    Use of timer   . . . . . . . . . . . . . . . . . . . . . . . . . . . . 24
    QuickBASIC Function Specifications   . . . . . . . . . . . . . . . . . 25
    Errors and Signals   . . . . . . . . . . . . . . . . . . . . . . . . . 25

    Installation   . . . . . . . . . . . . . . . . . . . . . . . . . . . . 27
    Application development considerations   . . . . . . . . . . . . . . . 27
    C-Compiler considerations  . . . . . . . . . . . . . . . . . . . . . . 27
    MicroSoft QuickBASIC compiler 4.5 Considerations   . . . . . . . . . . 27
    Building an EXE-file   . . . . . . . . . . . . . . . . . . . . . . . . 27
      C-language and DOS   . . . . . . . . . . . . . . . . . . . . . . . . 28
      C-language and BASIC   . . . . . . . . . . . . . . . . . . . . . . . 28
      C-language and OS2 1.3   . . . . . . . . . . . . . . . . . . . . . . 29

  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                                 Contents  ii


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
      C-language and OS2 2.0+  . . . . . . . . . . . . . . . . . . . . . . 30
    Storage and performance  . . . . . . . . . . . . . . . . . . . . . . . 30
      Memory Utilisation   . . . . . . . . . . . . . . . . . . . . . . . . 30
      Processor utilisation  . . . . . . . . . . . . . . . . . . . . . . . 30
    Comments, Remarks, Bug-reports   . . . . . . . . . . . . . . . . . . . 31

    Appendix A.  MKLAPI Internals  . . . . . . . . . . . . . . . . . . . . 32
    Multitasking   . . . . . . . . . . . . . . . . . . . . . . . . . . . . 32
    Reading M„rklin S88 encoders   . . . . . . . . . . . . . . . . . . . . 33
    Communications Interface Specification   . . . . . . . . . . . . . . . 35
    Problems with OS/2 COM[xx].SYS   . . . . . . . . . . . . . . . . . . . 37
    OS/2 and DOS differences   . . . . . . . . . . . . . . . . . . . . . . 38

    Appendix B.  Trace facility  . . . . . . . . . . . . . . . . . . . . . 40
    Trace records  . . . . . . . . . . . . . . . . . . . . . . . . . . . . 40
    Sample   . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 40

  | Appendix C.  M„rklin-Interface peculiarities   . . . . . . . . . . . . 41

    Appendix D.  Summary of changes  . . . . . . . . . . . . . . . . . . . 42
































  
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  (1)     This document is processed: on May 4, 1993 at 9:52 p.m.

  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                                Contents  iii


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  INTRODUCTION

                    Copyright (C) R. Hamerling, 1991, 1993
                             All Rights Reserved.
  



  WHAT IS MKLAPI?

  MKLAPI is a combination of:

  þ  a driver for buffered communications, automatic reading of M„rklin S88
     encoder-boxes, timer- and some other services.

  þ  a number of user callable routines for common elementary functions, with
     a comfortable high-level programming interface.

  So MKLAPI reliefs a programmer from 'low-level' tasks such as controlling
  the communication with the M„rklin-Interface, so that he can concentrate on
  the railroad-control logic.  This simplifies programming for
  model-railroads which are controlled via a M„rklin-Interface.  Internally
  it performs a kind of multi-tasking, which is highly desirable for this
  realtime environment ('proces control').


  PURPOSE

  The driver and API has been developed for the following purposes:

  þ  have an application programming interface (API) which is independent of
     the operating system (i.c. OS/2 or DOS).

  þ  provide a simple interface for a number of frequently used basic control
     functions such as sending commands to trains and switch points, and
     reading sensors.

  þ  allow the mainline to be written completely in high-level programming
     language (i.c. C-language or QuickBASIC).

  þ  obtain a buffered communications facility to the M„rklin-Interface,
     including automatic flow control as required by the M„rklin-Interface.

  þ  have 'background' tasks for a number of functions that should or could
     be performed independently and asynchronously from the mainline.

  þ  provide an accurate and efficient timer facility for time-dependent
     operations, events and interval-calculations.








  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                              Introduction  1


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  REALISATION

  This package offers a set of drivers with all the functionality of listed
  "Purpose" on page 1.  Although the OS/2-drivers and DOS-drivers are
  completely different implementations, due to the rather extreme differences
  in functionality provided by OS/2 and DOS for this type of environment, the
  mainline of your railroad control program may be unaware of the underlying
  operating system: the application programming interface is identical.

  You may read a number of minor differences in "OS/2 and DOS differences" on
  page 10.


  REGISTRATION

  This package is of the 'SHAREWARE' type: You may try it for a reasonably
  short time (max 3 months).  If you decide to use it for your own railroad
  control program, you may show your appreciation and become a 'registered
  user'.  After registration, I'll send you by mail:

  þ  A diskette (3-1/2", 720KB), with the following contents:
     ù  The most recent version of all the drivers.
     ù  Source-files (C-language) of a couple of sample programs provided as
        executables in the base package.

  þ  Complete and up-to-date printed documentation, as well as 2
     documentation files on the diskette:
     ù  A print-file, formatted for IBM Pro-Printer III.
     ù  A file in OS/2 INF format (VIEW-able as online documentation like the
        inline OS/2 Command Reference Manual).

  After registration you are allowed to distribute the driver as integral
  part of your own railroad control application programs.  The package (not
  the material you get after registration) may be distributed freely with
  under the following conditions:

  þ  it remains a separate and complete package
  þ  you do not apply changes of any kind
  þ  you do not make profit with it

  The registration fee is 45 Dutch Guilders or equivalent of 25 US-Dollars.
  Bare money is accepted as well, but foreign money only in the form of
  US-Dollar banknotes.

  Please send your comments and registration fee to:

       R. Hamerling
       Vianen-ZH,
       The Netherlands
       Postbank acct#: 2087285
       PC-Square: FIDOnet 2:512/4.1098

  Mention the purpose of your payment ("MKLAPI"), and the destination
  address!  MKLAPI-source is not included.


  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                              Introduction  2


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  FUNCTIONAL DESCRIPTION

  This chapter describes a possible use of this package.


  OVERVIEW

  The M„rklin-Interface-driver package is a set of functions to enable direct
  communications support in a program written in C-language or BASIC for the
  MicroSoft QuickBASIC compiler 4.5((2)) for the family of IBM Personal
  System/2 and compatibles.
  Please report problems with the driver as soon as you can.  and accompany
  your report with as much details as might be relevant.


  TERMINOLOGY

  In this document I use a number of terms which should probably be clarified
  first.

  Interface The M„rklin-Interface. (M„rklin partnumber 6050)

  Sensor    The M„rklin S88 encoder. (M„rklin partnumber 6088).  Sometimes
            also called sensor-box or encoder.

  Switch    The railroad facility, M„rklin K83 decoder (M„rklin partnumber
            6083) is used to control these switch points.



  FUNCTIONAL REQUIREMENTS

  The M„rklin-Interface-driver must provide the following functionality:

  þ  Possibility to send commands to the M„rklin-Interface in any sequence
     and mix.

  þ  Builtin buffered communication with the M„rklin-Interface.

  þ  Automatic flow control between PC and M„rklin-Interface.

  þ  Time-base (clock) for for time-dependent control, independent of
     hardware (processor) speed.

  þ  Automatic readout of sensor-boxes (M„rklin S88 encoder): the mainline
     must be able to obtain sensor positions instantaneously (without
     waittime).

  
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  (2)     Please note that this driver is delivered in the form of
          .OBJ-files, and therefore can be used only with compiled programs
          (other .OBJ-files).  QBASIC that comes with DOS 5.0 is not capable
          of producing an .OBJ file, you'll need the MicroSoft QuickBASIC
          compiler 4.5 to use this driver with BASIC programs.

  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                    Functional description  3


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  þ  Priority mechanism: mainline activities must be handled with higher
     priority than 'background' service processes.

  þ  Ability for emergency stops, regardless of the state of the program or
     the model railroad.



  PROVIDED FACILITIES

  To fulfil the functional requirements, a 'driver' has been built.  It
  contains a number of service-routines (and for DOS also hardware interrupt
  routines), and provides the following facilities:

  þ  Functions to send train and switch commands to the interface.

     Two macro's for output of resp. 1 or 2 consecutive characters (the so
     called 1-byte or 2-byte commands).  With the 2-byte form the subroutines
     ensure that the 2 characters are sent as 2 consecutive characters (not
     interrupted by a 'background' task).

  þ  Functions to read sensors (S88-boxes).

     This can either be done by immediate reading the status of the last
     polling operation (if polling started).  "Reading M„rklin S88 encoders"
     on page 33 contains details about this mechanism.

     If the mainline is sending a command to the M„rklin-Interface, polling
     is automatically suspended (the command is treated with higher
     priority).

  þ  A 'shadow' of the system timer, but expressed in milliseconds since
     program start.  This timer has with the OS/2-driver of MKLAPI a
     precision of 31.25 msecs, using standard OS/2 facilities (the timer
     tick).  With the DOS-driver of MKLAPI the posibilities of the hardware
     PC timer are explored, giving a precision of 1 millisecond.

  þ  A trace facility is built in for easy program debugging.  All output to
     the interface can [optionally] be traced (OS/2 only) and formatted
     later.



  DELIVERABLES

  The shareware components of the M„rklin-Interface-driver package are:

| þ  This documentation file: MKLAPI.DOC.
| þ  Header file for C-language: MKLAPI.H with function prototypes, data- and
|    macro- definitions.
| þ  Include file for QuickBASIC: MKLAPI.INC with function prototypes.
| þ  2 OS/2-object decks, MKLAPI2.OBJ (16-bits OS/2 version) and MKLAPI3.OBJ
|    (32-bits OS/2 version), with a buffered multitasking communication
|    interface, polling, timer-support and trace facility.
| þ  2 DOS-object decks for C-language programs, SMKLAPI.OBJ and LMKLAPI.OBJ,

  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                    Functional description  4


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
|    with the same functionality as the OS/2 drivers, (but without a trace
|    facility).  SMKLAPI is the object deck to be linked with your SMALL
|    memory model program, LMKLAPI.OBJ is for LARGE memory model C-language
|    programs.  LMKLAPI.OBJ is also used for QuickBASIC programs.
  þ  TRAIN.EXE and TRAIN2.EXE, which are ready to run sample programs for a
     DOS and OS/2 environment respectively.  See "Sample programs" on page 8
     for some characteristics of these programs.
  þ  MKLTRFMT.EXE, utility to interpret (format) the recorded trace file.

  The registration package consists of:

  þ  Sources (in C-language) of a sample train control program that makes use
     of the M„rklin driver, usable for OS/2 and DOS ('fullscreen'
     application)
  þ  All include and header files
  þ  All MAKE and DEF files, used for compilation with MicroSoft C-compiler
     6.00a or equivalent, IBM C SET/2 compiler for 32-bits programs and
     MicroSoft QuickBASIC compiler 4.5 for QuickBASIC programs.



  PREREQUISITES

  The package has been built with the following assumptions:

  þ  Your PC-hardware is 100% compatible with the productline of IBM Personal
     Computers (PC, PC/XT, PC/AT, and all current models of the Personal
     System/2 family), in particular the asynchronous communication adapters,
     their port addresses, etc. and the hardware timer.

  þ  The operating system is either OS/2 1.2 or higher, or PC-DOS 2.1 or
     MS-DOS 2.1 or higher.  The package has been tested only with IBM PC/DOS
     version 4.0 and 5.0, and with OS/2 version 1.3 and 2.0 (in OS/2
     session).

  þ  Your (16-bits) C-programs (OS/2 and DOS) will be compiled with MicroSoft
     C-compiler 6.00a.  For 32-bits C-programs IBM C SET/2 compiler is
     assumed.  There may be some specific requirements on system hardware and
     software for these.  Maybe Borland Turbo C compiler will work as well,
     but this has not been tested.

  þ  Your BASIC programs will be compiled with the MicroSoft QuickBASIC
     compiler 4.5.



  RESTRICTIONS AND LIMITATIONS

  The following restrictions apply:

  þ  One single port can be used between open and close of the COM-port to
     the M„rklin-Interface, all other functions apply to the port chosen at
     open-time.

  þ  The transmit buffer of the DOS-driver is 2048 bytes long, for OS/2 it

  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                    Functional description  5


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
     depends on COM[xx].SYS, or substitute.

  þ  Received data is transferred immediately to the sensor-array (64 bytes).

  þ  When the mainline is sending data to the M„rklin-Interface and a
     buffer-full situation arises, the data will be discarded.  However it is
     very unlikely that this will happen in real life.

  þ  If you read a sensor-box outside the polling-range, the response is
     undefined.



  TESTS

  The drivers have been tested by the author with combinations of the
  following hardware and software:

  þ  model railroad equipment:
     ù  M„rklin Combined Control
     ù  3 M„rklin Digital locs
     ù  3 M„rklin K83 decoders, each connected to 4 switch points
     ù  1 M„rklin S88 encoder, with railroad-section sensoring

  þ  computer hardware:
     ù  IBM PC/AT-3 (80286/8) with IBM serial-parallel adapter
     ù  IBM PS/2 model 80 (80386/16) with standard serial port
     ù  IBM PS/2 notebook N51SLC (80386SLC/16) with standard serial port and
        second serial port
     ù  IBM compatible 80486/33 with multi-I/O card

     Note: The DOS-drivers are written in 8086/8 Assembler and should also
     work on XT-type systems.

  þ  Operation Systems:
|    ù  IBM OS/2 2.0: 32-bits mode with MKLAPI3.OBJ, 16-bits mode with
|       MKLAPI2.OBJ, DOS-session with LMKLAPI.OBJ
|    ù  IBM OS/2 1.3: MKLAPI2.OBJ
|    ù  IBM PC/DOS 5.0: LMKLAPI.OBJ with QuickBASIC and C-language

  Note: Not all combinations of hardware and software have been tested, but
  it is not likely that any viable combination will not work.














  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                    Functional description  6


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  C-LANGUAGE FRAMEWORK

  A typical model railroad control program with this driver may look like:


       #include "mklapi.h"

       mklopen(1,2400);                  /* open COM1: */
       mklpoll(5);                       /* 5 S88 boxes in yard */
       while (key != ESC) {              /* end program from keyboard */
         if (kbhit()) {                  /* keyboard input */
           if (key = getch()) {          /* normal key (incl alt-numpad) */
             switch(key) {
               case '?':   - - - - -     /* your key, your function */
                           break;
               case ESC:   break;        /* nothing now, exit program */
               default:    fprintf(stdout,"%c",BEL);
                           break;        /* unsupported normal key */
               }
             }
           else {                        /* 'special' key */
             switch(key = getch()) {     /* extended character */
               case PgDn:   - - - - -    /* your 'extended' key function */
                           break;
               default:    fprintf(stdout,"%c",BEL);
                           break;        /* unsupported 'extended' key */
               }
             }
           }
         for (i=0; i<MAXTRAIN; i++) {    /* scan train matrix */
           - - - - -                     /* train control function */
           }
         for (i=1; i<5, ++i) {           /* scan S88 boxes */
           mklgetsn(i);                  /* read sensor bits */
           - - - - - -                   /* process changes */
           }
         if (!(mkltime()%5000)) {        /* every 5 seconds */
           - - - - -                     /* anything else */
           }
         mklsleep(25);                   /* give up remainder of timeslice */
         }
       mklflush();                       /* wait until output sent */
       mklclose();                       /* terminate */

  Note: Above code is just a framework to show the general setup of a model
  railroad control program using the M„rklin-Interface.










  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                    Functional description  7


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  QUICKBASIC FRAMEWORK

  An equivalent framework in QuickBASIC might look like:


       ' $INCLUDE: 'MRKAPI.INC'

       rc = mklopen(1,2400);
       mklpoll(5);
       key$ = INKEY$
       while key$ <> ESC$
         select case key$
           case '?'
              - - - - -
           case ESC
              - - - - -
           case else
             print "error key"
         end select
         for i=0 to MAXTRAIN
           - - - - -
         next i
         for i=1 to 5
           mklgetsn(i)
           - - - - - -
         next i
         if MOD(mkltime,5000) < 50 then
           - - - - -
         end if
         mklsleep(25)
         key$ = INKEY$
       wend
       mklflush;
       mklclose;

  Note: This code may not be true and workable QuickBASIC!

  The file MKLAPI.INC contains the DECLARE lines for all functions contained
  in LMKLAPI.OBJ.  It should be included in a QuickBASIC program to obtain
  the correct calling conventions and activates syntax checking by the
  MicroSoft QuickBASIC compiler 4.5.  Subsequently the file LMKLAPI.OBJ
  should be linked with your QuickBASIC program to include the MKLAPI
  functions and subroutines.


  SAMPLE PROGRAMS

  After registration you will receive the sources a sample (C-language)
  program:

  þ  Control of 8 trains and several other possibilities, with the following
     details:
     ù  Speed is controlled from the computer keyboard with arrow (cursor)
        keys: right-key is faster, left-key is slower, up-key is maximum for
        this train, down is maximum backward for this train.

  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                    Functional description  8


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
     ù  The train for which the command is meant is selected with a
        number-key (program provides control for trains 1 through 8).  The
        corresponding loc-address and other train properties are in a matrix
        (with individual entries for each train), such as minimum and maximum
        speed in M„rklin Central Control values.  The train addresses that
        are programmed are 10 for train 1, 20 for train 2, etc until 80 for
        train 8.
     ù  The speed-control is indirect: you tell the system the program
        loc-speed, the program does mass-simulation ('slow' increase and
        decrease of speed).  The parameters for enertia simulation are part
        of the train definitions.
     ù  For each train its address, desired and actual train speed are
        displayed (in color).  Direction changes are buffered and automatic.
     ù  The display also indicates direction and whether the extra function
        is 'on' or 'off'.

  þ  Control of 4 M„rklin K83 decoder for 16 railroad switch points.  For
     each switch the position ('normal' or 'bound' in color) and its address
     is displayed.  The keys are A-P for adresses 253-256, and 1-12
     respectively.

  þ  Polling of M„rklin S88 encoder each with 16 sensors (or isolated
     railroad sections).  The position is displayed real time, nothing but
     displaying is done with the information.  2 M„rklin S88 encoder-boxes
     are being polled.

  þ  Sensor 16 of M„rklin S88 encoder-box 1 is designated for speed
     measurement.  The display shows the time (in milliseconds) between 2
     successive 'OFF-ON' transitions.  If there is 1 train running and moving
     along the same road, this facility can be used for calibrating speed
     calculations for each speed-command-value.

  þ  Other keys:
     Insert    Set Function 'on'
     Delete    Set Function 'off'
     End       Stop polling
     Home      Restart polling
     F3        Stop the program (has to be entered twice consecutively)
     Esc       Emergency Stop (issues the M„rklin Central Control STOP
               command)
     Enter     Resume (issues the M„rklin Central Control GO command)

  The program may be started with 2 numeric parameters:

  1. the first parameter indicates the COM-port to be used (1 for COM1, 2 for
     COM2, etc.), The default is COM1.
  2. The second parameter indicates the number of M„rklin S88 encoder-boxes
     to include in the polling mechanism.  The default is 2.








  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                    Functional description  9


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  OS/2 AND DOS DIFFERENCES

  The OS/2-drivers differ from the DOS drivers:

  þ  The OS/2-drivers are written in C-language, the DOS drivers in
     Assembler.

  þ  The OS/2-driver makes use of the services provided by the standard OS/2
     communications driver COM02.SYS (for PS/2) or COM01.SYS for others under
     OS/2 version 1.3, and COM.SYS for OS/2 version 2.0.  The DOS driver
     interfaces directly with the PC hardware.

  þ  The OS/2-driver makes use of the standard OS/2 facilities for
     multithreading (task signalling is done with semaphores).  The DOS
     driver performs a form of multi-tasking, driven by interrupts (the
     COM-port hardware and the standard DOS timer tick).

  þ  The DOS-drivers explore the possibilities of the hardware timer of the
     PC to obtain a accurate time values when needed.  With the DOS
     timer-tick of 55 msec the average deviation would be about 28 msec.
     OS/2 does not allow access to the hardware by 'normal' applications,
     therefore the OS/2-drivers use standard OS/2 function calls.  Since the
     OS/2 timer tick is 31.25 msec, the average deviation will be about 16
     msecs.

  The sample program under DOS chokes the processor (takes all the cycles
  that are available).  This is OK in a typical single-task environment, but
  not very suitable for a multitasking system.  Under OS/2 a very simple
  solution for this problem is to insert  for example a DosSleep(30L) at the
  end of the infinite (keyboard-) loop.  There may be better solutions.


























  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                   Functional description  10


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  SPECIFICATIONS

  This chapter describes the use of the provided facilities.


  AVAILABLE FUNCTIONS

  The following user callable functions are provided:

  mklopen         Start communication with the M„rklin-Interface and the
                  background tasks.
  mklclose        Stop background tasks and shutdown the communication with
                  the M„rklin-Interface.
  mklputc         Transmit 1 or 2 character-commands to the
                  M„rklin-Interface.
  mklflush        Wait until all data transmitted.
  mklpurge        Discard remaining data in output buffer.
  mklpoll         Start or stop polling of M„rklin S88 encoder boxes.
  mklgetsn        Obtain the status of 1 M„rklin S88 encoder (when polling
                  active).
  mklstop         Set M„rklin-Interface in 'stop'-state and stop polling
  mklgo           Set M„rklin-Interface in 'go'-state and (optionally) resume
                  polling.
  mklmsecs        Give accurate time in milliseconds since program start
                  (only in DOS-drivers).
  mkltime         Give time of last timer tick in milliseconds since program
                  start.
| mklstats        Provide statistics (activity counters).
| mklsleep        Pause for a certain time (and give up the remainder of a
|                 time slice when running in a multitasking environment).
| mklsound        Sound generator like BASIC sound or OS/2 DosBeep()
  mkltrace        Start or stop recording data that is being sent to
                  M„rklin-Interface  (only in OS/2-drivers).

  The next sections contain the specifications of available functions of the
  M„rklin-driver, in alphabetical sequence.

  Note: The descriptions for C-language and QuickBASIC are given both, but in
  the text mainly the C-language notations are used.


  MKLCLOSE

  Name            mklclose - close communications with the M„rklin-Interface.

  C-language

                    #include "mklapi.h"
                    void mklclose(void);

  QuickBASIC

                    ' $INCLUDE: 'MKLAPI.INC'
                    DECLARE SUB MKLCLOSE CDECL ()


  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                           Specifications  11


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  Description     The close-routine disables the communications task of the
                  driver.  It should be called before termination your
                  program.  Transmits and receives that were in progress will
                  be terinated, data might be lost.

  Return value    Nothing.

  Related functions "mklopen" on page 15

  Warning: mklclose() is not a trivial function!  It must be used when
  mklopen() has been called succesfully (under DOS).  Otherwise your system
  may enter a hang-up situation when for no matter what reason your
  communications port gives an interrupt.  So terminate your program always
  'neatly' (so intercept Ctrl-Break in your program to prevent uncontrolled
  program termination)!



  MKLFLUSH

  Name            mklflush - flush all buffered output.

  C-language

                    #include "mklapi.h"
                    int mklflush(void);

  QuickBASIC

                    ' $INCLUDE: 'MKLAPI.INC'
                    DECLARE FUNCTION FLUSH% CDECL ()

  Description     Wait until all output is sent to the M„rklin-Interface.  In
                  other words: wait for empty transmit buffer before
|                 returning to caller.

|                 When buffered data is apparently not transmitted anymore,
|                 the remaining bytes in the transmit buffer will be purged
|                 and the purge statistics are updated accordingly.

| Return value    Depending on success:
|                 þ  0   when no more bytes to transmit (buffer empty)
|                 þ  >0  number of bytes not transmitted (purged) buffer.
                  þ  -1 (DOS) last byte in hardware buffer was not
                     transmitted

  Related functions "mklpurge" on page 16









  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                           Specifications  12


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  MKLGETSN

  Name            mklgetsn - get bit-pattern of a single M„rklin S88 encoder.

  C-language

                    #include "mklapi.h"
                    unsigned short int mklgetsn(short int sensor);

  QuickBASIC

                    ' $INCLUDE: 'MKLAPI.INC'
                    DECLARE FUNCTION MKLGETSN% CDECL (BYVAL SENSOR%)

  Description     Get a single sensor-box word (16 bits) from the sensor
                  array.

                  This function does not generate any action to the
                  M„rklin-Interface and returns the bitsetting immediately.
                  Polling will have to be started first, with mklpoll(),
                  before the reading of sensors will give meaningful results.
                  Reading outside the range 1..31, or higher than the value
                  as specified with the latest mklpoll(maxsensor) or
|                 mklgo(maxsensor), will give unpredictable results.

|                 The M„rklin-Interface is always read with 'reset'.  The
|                 resulting 1-bits ('on'-switches) are cumulated until a
|                 mklgetsn() is called for a specific S88.  The caller
|                 obtains the cumulative bit-setting, but the sensor word is
|                 refreshed immediately with the results of the last read
|                 command.  Depending on the type of switche used on the
|                 model railroad, and the frequency in which mklgetsn() is
|                 issued by the mainline, it may be necessary to issue
|                 mklgetsn() twice.  See for a further explanation: "Reading
|                 M„rklin S88 encoders" on page 33.

  Return value    A 16-bit word containing the current switch positions.



  MKLGO

  Name            mklgo - send the 'go' command.

  C-language

                    #include "mklapi.h"
                    int mklgo(short int maxsensor);

  QuickBASIC

                    ' $INCLUDE: 'MKLAPI.INC'
                    DECLARE FUNCTION MKLGO% CDECL (BYVAL MAXSENSOR%)

  Description     Send the 'go'-command (ASCII 96) to the M„rklin-Interface

  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                           Specifications  13


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
                  immediately.

                  The value of MAXSENSOR has the same meaning and effect as
                  in mklpoll (see "mklpoll" on page 16).  Polling will be
                  resumed if a non-zero parameter is specified.

                  OS/2: The go-command is sent via a DevIOCtl operation (send
                  immediate), and will be followed by a simulated XON.  If
                  there was buffered output (before the stop-state or after
                  entering stop-state under OS/2 2.0), it will be transmitted
|                 now.

|                 OS/2: If the 'go'-command could not be sent, for example if
|                 the Interface is not ready to accept data, a permanent low
|                 beep will be heard until the 'go'-button on M„rklin Central
|                 Control is pressed.  If an other error occured, mklgo will
|                 return an error code.

                  DOS: The go-command is send just as regular data.  The
                  returncode is always zero.

  Return value    Nothing.

  Related functions "mklstop" on page 21, "mklpoll" on page 16



  MKLMSECS

  Name            mklmsecs - obtain time since program start in milliseconds.

  C-language

                    #include "mklapi.h"
                    unsigned long int void mklmsecs(void);

  QuickBASIC

                    ' $INCLUDE: 'MKLAPI.INC'
                    DECLARE FUNCTION MKLMSECS& CDECL ()

  Description     (DOS only!) Returns the exact time in milliseconds after
                  program start without waiting for the next timer tick.
                  This might be useful for more accurate timing for special
                  purposes.  Of course it takes some time to execute the
                  necessary instructions to read the timer and format the
                  information.  On faster systems mklmsecs() gives the time a
                  little more precise than on slower systems, but even on
                  relatively slow systems it is much more precise than
                  probably needed for the purpose of mode railroad control!
                  If this very high precision is not needed, then use the
                  function mkltime().

                  (OS/2) This function is 100% equivalent to mkltime().


  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                           Specifications  14


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  Return value    Time in milliseconds after program start.

  Related functions "mkltime" on page 22



  MKLOPEN

  Name            mklopen - open communications line

  C-language

                    #include "mklapi.h"
|                   int  mklopen(short int port, short int speed);

  QuickBASIC

                   ' $INCLUDE: 'MKLAPI.INC'
|                  DECLARE FUNCTION MKLOPEN CDECL (BYVAL PORT%, BYVAL SPEED%)

  Description     Open and initialise communications port driver, high
                  resolution timer (DOS only), and set all statistics
                  counters to zero.  The port-parameter may have a value of 1
|                 to 4, indicating COM1: to COM4:.  With DOS the port
|                 addresses are obtained from BIOS, with OS/2 the COM[xx].SYS
|                 device driver has them.  The interrupt levels are IRQ4 for
|                 COM1 and COM3, IRQ4 for COM2 and COM4.  As you see COM3 may
|                 conflict with COM1 (and COM2 with COM4).  You cannot use
|                 conflicting interrupt levels at the same time in most
|                 computers.

                  Any port will always be initialised with 8-bit, no-parity,
                  2 stop-bits.  The speed parameter should specify 2400,
                  since it is the only speed supported by the
                  M„rklin-Interface.  Maybe later other values?

                  The counterpart of mklopen() is mklclose(), which should be
                  called before finishing your (DOS-) program.

| Return value    Depending on success:
|                 þ  0     - port opened succesfully
|                 þ  32    - port probably occupied by another device
|                 þ  110   - port not available
|                 þ  other - see OS/2 or DOS documentation

|                 With OS/2 the port is opened by a separate thread.  When
|                 the port could not be opened, the whole process will be
|                 terminated.

  Related functions "mklclose" on page 11, "mklstats" on page 19






  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                           Specifications  15


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  MKLPOLL

  Name            mklpoll - start periodic reading of M„rklin S88 encoder.

  C-language

                    #include "mklapi.h"
                    void mklpoll(unsigned int maxsensor);

  QuickBASIC

                    ' $INCLUDE: 'MKLAPI.INC'
                    DECLARE SUB MKLPOLL CDECL (BYVAL MAXSENSOR%)

  Description     M„rklin S88 encoderboxes 1..MAXSENSOR will be read by a
                  'background' process.

                  When starting the polling process a 'read with reset' is
                  issued.  The responses of the read-operation are stored in
                  sensor-arrays.  Each word of the array can be read
                  individually at any time with mklgetsn().  See for details
                  "Reading M„rklin S88 encoders" on page 33.

  Return value    Nothing

  Related functions "mklgo" on page 13 and "mklgetsn" on page 13



  MKLPURGE

  Name            mklpurge - purge output buffer

  C-language

                    #include "mklapi.h"
                    void mklpurge(void);

  QuickBASIC

                    ' $INCLUDE: 'MKLAPI.INC'
                    DECLARE SUB MKLPURGE CDECL ()

  Description     Discard current contents of output buffer.  If the output
                  buffer does contain any characters, these are not sent tot
                  the Interface.  After purging the current contents, control
                  is immediately returned.  See also "mklflush" on page 12.

                  Note: This function is currently available in the driver
                  for DOS.

  Return value    Nothing.

  Related functions "mklflush" on page 12


  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                           Specifications  16


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  MKLPUTC

  Name            mklputc - send 1 or 2 characters to the interface

  C-language

                    #include "mklapi.h"
                    int mklputc(unsigned int word);

  QuickBASIC

                    ' $INCLUDE: 'MKLAPI.INC'
                    DECLARE FUNCTION MKLPUTC% CDECL (BYVAL WORD%)

  Description     Send 1 or 2 characters to the M„rklin-Interface.  The
                  'word' is interpreted as two contiguous characters.  The
                  low order byte of the word is sent first, followed by the
                  high-order byte.  If the high is not sent when zero.  The
                  exception to this rule is: if the first byte is a
                  switch-command (ASCII 33 or 34), then the second byte will
                  be sent, even when zero.

                  This function returns immediately, and does not wait for
                  the bytes to be actually transmitted to the interface.  The
                  communications task will take care to send the buffered
                  character(s) to the M„rklin-Interface.

                  Coding example to signal speed 8 to loc 27:

                      rc = mklputc( 27*256 + 8)

                  For C-language programs it is highly recommended to use the
                  provided macro's for sending 1 or 2 character commands (see
                  "Macro Specifications" on page 23).

                  Warning: When there is no room in the output buffer, then
                  both  characters will be discarded.

  Return value     0   character(s) are accepted by the driver.

                  -1   characters NOT accepted: output discarded.

  Note: If you use mklputc() while the driver is in 'stop-state' (see
  "mklstop" on page 21):

  þ  the OS/2-drivers issue a short high-pitch beep.  With OS/2 2.0 the data
     might be buffered and transmitted after mklgo().  This depends on the
     used device driver for the COM-port.  COM[xx].SYS does not buffer, but
     SIO.SYS does (until its 4KB buffer is full).
  þ  the DOS-drivers do not generate a warning and will discard the data
     until the stop-state is left via a call to mklgo().





  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                           Specifications  17


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  MKLSLEEP

| Name            mklsleep - pause some time and yield processor

| C-language

|                   #include "mklapi.h"
|                   void mklsleep(short int pause);

| QuickBASIC

|                   ' $INCLUDE: 'MKLAPI.INC'
|                   DECLARE SUB MKLSLEEP CDECL (BYVAL PAUSE%)

| Description     This function provides two facilities:
|                 þ  It does not return to the caller before the indicated
|                    pause-interval (im milliseconds) has expired.
|                 þ  In a multitasking environment (OS/2, DesqView, Windows)
|                    it releases the processor for this task.

|                 In the OS/2-driver this function is equivalent to
|                 DosSleep().  In the DOS-driver it is implemented as a loop
|                 with an imbedded test for multitasking, in the OS/2-driver
|                 as DosSleep().

|                 The pause should be specified in milliseconds, and thus
|                 cannot exceed about 32 seconds!  The specified
|                 pause-interval is rounded to the next timer tick, but may
|                 be even larger when the multitasker decides not to give
|                 control yet to this task after expiration of the interval!

                  When running a DOS-program in a multitasking environment
                  (OS/2, Desqview, Windows, etc.), it is desirable to give
                  control back to the multitasker, when the program does not
                  need the processor for some time.  This part of mklsleep()
                  is experimental, it may not work with all multitaskers.
                  The use of mklsleep is not absolutely needed with
                  pre-emptive multitaskers (like OS/2), but is strongly
                  recommended.  In all cases it reduces CPU utilisation and
                  leaves processor time for other tasks.

  Return value    Nothing.



  MKLSOUND

  Name            mklsound - give a 'beep'

  C-language

                    #include "mklapi.h"
                    void mklsound(short int freq, short int time)

  QuickBASIC

  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                           Specifications  18


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
                    ' $INCLUDE: 'MKLAPI.INC'
                    DECLARE SUB MKLSOUND CDECL (BYVAL FREQ%, BYVAL TIME%)

  Description     Produces a beep-tone with frequency 'freq' expressed in
                  Hertz, during a period 'time' expressed in milliseconds.
                  The tone is played in background, all processing continues
                  without delays or slowdown of the system.

                  DOS: A beep can be stopped prematurely by calling
                  mklsound() with a zero frequency, or by mklclose().  A beep
                  can be changed by mklsound() with a different frequency.
|                 This will stop any previous beep.

|                 OS/2: mklsound is implemented as DosBeep and thus behaves
|                 exactly like it.  It is included in the OS/2 driver only
|                 for source compatibility between OS/2 and DOS programs
|                 using MKLAPI.

  Return value    Nothing.



  MKLSTATS

  Name            mklstats - obtain content of statistics counter.

  C-language

                    #include "mklapi.h"
                    long int mklstats(int counter);

  QuickBASIC

                    ' $INCLUDE: 'MKLAPI.INC'
                    DECLARE FUNCTION MKLSTATS& CDECL (BYVAL COUNTER%)

  Description     Obtain value of an internal counter in MKLAPI for
                  statistical purposes.  All counters will be reset to zero
                  with mklopen(), and can also be reset by a user program
                  through specification of 0 (zero) as parameter.

                  To read a counter specify a number in the range: 1 to 6.
                  The counters (by number) have the following contents:
                  1   Number of accepted commands, including polling-commands
                      (commands to read S88's).  Since the we use a buffering
                      mechanism, not all of these commands may have been
                      transmitted actually!
                  2   Number of internally generated commands to read S88's
                      ('polls').
                  3   Number of commands that have been discarded.  Reasons
                      may be:
                      þ  system is in 'stop-state'
                      þ  transmit buffer is full
                  4   Number of bytes that were transmitted.  With the
                      DOS-driver these bytes are actually transmitted to the

  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                           Specifications  19


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
                      COM-port, with OS/2 they were accepted by the device
                      driver of the COM-port.
                  5   Number of received bytes (most likely as result
                      commands to read S88's).
                  6   Number of bytes that were purged (discarded after first
                      being accepted, but before actually being transmitted
                      to the M„rklin-Interface).  Reasons may be:
                      þ  there were commands buffered while mklstop() was
                         called
                      þ  mklflush() could not complete (timeout)
                      þ  commands were in the transmit buffer during a call
                         to mklpurge()

                      Discarded commands are not counted as 'purged', since
                      they were not accepted and never put into the transmit
                      system!

                      Note: Purging is not supported in the OS/2-drivers, so
                      this counter should remain zero with OS/2 programs.

                  Counters in the range 1 to 6 can be considered as permanent
                  feature of MKLAPI.  Counters in the range 7 to 15 are
                  mainly for debugging purposes.  The description below is
                  for information purposes only, do not use them in your
                  program, as they may be incorrect, their meaning be changed
                  in a next version of MKLAPI, or may not be active at all in
                  the distributed drivers (for performance reasons).
                  7   DOS: Number of calls to mklputc while the driver's
                      transmit buffer was empty.
                  8   DOS: Number of calls to mklputc while the CTS signal is
                      'high'.
                  9   DOS: Number of calls to mklputc while the
                      hardware communications buffer was empty.
                  10  DOS: Number of calls to mklputc whereby the first or
                      only byte had to be put in the driver's communications
                      buffer.
                  11  Number of calls to mklputc with a request for 2 bytes
                      (second character always buffered).
                  12  DOS: Total number of interrupts processed by the
                      interrupthandler for the asynchronous communications
                      port.
                  13  DOS: Number of THRE interrupts.
                  14  DOS: Number of MSR interrupts (number of CTS signal
                      changes).
                  15  DOS: Situations with a pending interrupt after a
                      previous interrupt was processed.

                  Specification of a counter number outside the indicated
                  range will give unpredictable results.

  Return value    Contents of the specified counter (zero after reset).

  Related functions "mklopen" on page 15



  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                           Specifications  20


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  MKLSTOP

  Name            mklstop - send the 'stop' command.

  C-language

                    #include "mklapi.h"
                    int  mklstop(void);

  QuickBASIC

                    ' $INCLUDE: 'MKLAPI.INC'
                    DECLARE FUNCTION MKLSTOP% CDECL ()

  Description     Send the 'stop'-command (ASCII 97) to the M„rklin-Interface
                  immediately.  If polling was active at the time, it will be
|                 stopped.

|                 þ  OS/2:  A simulated XOFF command is used to indicate the
|                    COM-driver to hold yet buffered data.  The stop-command
|                    is then sent via a 'send-immediate' operation, ahead of
|                    data that might be in the transmit buffer.  The transmit
|                    buffer is NOT purged, held data is preserved and sent
|                    after a 'go'-command.

|                    You may hear a low beep while the mklstop operation is
|                    waiting to get access to the M„rklin-Interface.  If an
|                    other error occured, mklstop will return an error code.

|                 þ  DOS: The transmit buffer is purged and the stop-command
|                    is then sent as regular data.  New output is not
|                    accepted anymore (it will be discarded).

                  Warning: The 'stop' command could be sent by the mainline
                  directly,  but then would bypass the administrative
                  functions of the driver.  Any train or switchpoint control
                  command received by the M„rklin-Interface will cause a
                  permanent drop of the CTS signal, making the control over
                  the railroad from the computer permanently
                  unavailable.  The only possibility to resume control then
                  is by manually hitting the 'go' key on the M„rklin Central
                  Control.

                  Note: The timer does not stop with a mklstop().  This may
                  cause strange effects from time-dependent calculations in
                  your mainline!

                  The 'stop' command might interfere with a 2-byte command of
                  which the first byte was already transmitted, but the
                  second byte not!  In that case the 'stop' would not be
                  recognised by the M„rklin-Interface.  Two consecutive
                  'stop'-commands will prevent the acceptation by the
                  M„rklin-Interface of any further commands from the
                  computer.  To make sure that the 'stop' command will be
                  processed by the M„rklin-Interface, with with the least

  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                           Specifications  21


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
                  inconvenience, MKLAPI precedes the 'stop'-command with a
                  'go'-command:
                  þ  If there was no command in transmission, then it won't
                     harm.
                  þ  If a 'broken' 2-byte command was in progress, then the
                     'go'-byte will be interpreted by the M„rklin-Interface
                     as the second byte.  This will probably have a different
                     effect than was foreseen, but since a 'stop' will
                     follow, this will be of minor importance.

                  A secundary effect of this setup is that it allows the
                  mainline to call mklstop() more than once.  The
                  intermediate 'go' ensures that the M„rklin-Interface
                  doesn't block permanently.

  Return value    Error code

  Related functions "mklgo" on page 13



  MKLTIME

  Name            mkltime - obtain time since program start in milliseconds.

  C-language

                    #include "mklapi.h"
                    unsigned long int mkltime(void);

  QuickBASIC

                    ' $INCLUDE: 'MKLAPI.INC'
                    DECLARE FUNCTION MKLTIME& CDECL ()

  Description     Returns the time in milliseconds after program start since
                  it was updated with the last timer 'tick' (OS/2: 31.25
                  msecs, DOS: 55 msecs).

                  This is a little less accurate than mklmsecs, but consumes
                  also less processor cycles.

  Return value    Time in milliseconds after program start.

  Related functions "mklmsecs" on page 14



  MKLTRACE

  Name            mkltrace - start or stop trace

  C-language

                    #include "mklapi.h"

  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                           Specifications  22


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
                    void mkltrace(short int signal);

  QuickBASIC      trace facility not provided in DOS drivers

  Description     Start or stop tracing of all data that is being sent to the
                  M„rklin-Interface and record the information, including a
                  timestamp into the file MKLAPI.TRC.

                  When signal is NOT zero, then tracing will be started, or
                  restarted (old trace data will be discarded in that case).
                  When signal is zero the trace is stopped and the trace file
                  closed.

                  It is my intention to replace this 'on/off' switch with a
                  trace level facility (selection of events or data to be
                  traced).

                  Note: Since a buffered communications interface is used,
                  the recording of trace data takes place at the moment the
                  data is sent to the buffer.  So the timestamp does not
                  reflect the exact transmission time.  Especially at moments
                  when M„rklin-Interface does not accept data (for example
                  when it is transmitting M„rklin S88 encoder-data), there
                  may be a significant time difference!

                  The utility MKLTRFMT.EXE can be used to produce a formatted
                  trace report.  All commands are printed hexadecimal and
                  interpreted.

                  See for details about the trace facility and a sample
                  output: "Appendix B.  Trace facility" on page 40.

  Return value    Nothing.

  Note: Tracing is not provided by the DOS-drivers, but a dummy function is
  provided for combined OS/2 and OS/2 programs.


  MACRO SPECIFICATIONS

  A number of C-language only macro's is provided to make specification of
  some function-calls a little more simple, and to take care of possibly
  needed data conversion.


  MKLPUT1C

  Name            mklput1c - send a single character to the interface.

  Usage           #include "mklapi.h"

                  void mklput1c(char);

  Prototype in    mklapi.h


  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                           Specifications  23


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  Description     Macro to send a single character in the output buffer.  The
                  macro will expand into a mklputc().

  Return value    See "mklputc" on page 17.



  MKLPUT2C

  Name            mklput2c - send two characters to the interface.

  Usage           #include "mklapi.h"

                  void mklput2c(char1,char2);

  Prototype in    mklapi.h

  Description     Macro to send two consecutive character in the output
                  buffer.  The characters will guaranteed be sent in the
                  given order, without the risk of intervening characters by
                  the polling mechanism.  The macro will expand into a
                  mklputc().

  Return value    See "mklputc" on page 17.



  USE OF TIMER

  At program start with mklopen(), the system time is taken as base for the
  functions mkltime and mklmsecs.  These functions return a value in
  milliseconds after mklopen().

  The OS/2-driver uses standard OS/2 facilities, which will allow a precision
  of about 16 msecs (the time is updated in OS/2 control blocks every 31.25
  msecs).

  The DOS-driver uses the system hardware to obtain the system time.  This
  allows a precision of 1 msec (with the function mklmsecs()).  The function
  mkltime() gives a precision of about 28 msecs, and takes less machine
  instructions, which might be sufficient for most purposes.

  The use of this timer facility provided by the MKLAPI-drivers has the
  following advantages:

  þ  It is independent of system (processor) speed and other tasks running in
     your system.  Many sample programs use some kind of processing loop to
     obtain a 'wait'-period, which might be dependent on processor speed and
     'choke' the processor, during which time no other useful work is
     possible, or at least it is pretty complicated.

  þ  It is available with very little processor cycles, so it is not needed
     to call a 'universal' compiler-provided timer routine, which are
     generally much more cycle consuming.


  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                           Specifications  24


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  The timer can be used for example for:

  þ  The application of an event-queue (for timed operations).
  þ  'Wait'-intervals during without programming a loop.
  þ  Simulation of train mass (inertia) through gradually increasing or
     decreasing loc-speed.

  If you register this package, you'll receive a sample program which makes
  use of this feature.

  It is recommended to use mklsleep() in cyclic operations when running in a
  multitasking environment sucha as Windows, DesqView or in a DOS-session
  under OS/2.


  QUICKBASIC FUNCTION SPECIFICATIONS

  The functionality of the M„rklin-driver for QuickBASIC is the same as for
  the drivers for C-language.  However the following should be noted:

  þ  BASIC does not allow the underscore-sign ("_") in names, as is very
     common in C-language.  Therefore the FUNCTIONS and DATA fields in the
     M„rklin-driver for QuickBASIC have been adapted a little to BASIC
     conventions since in 0.9 of these drivers.  All other differences are
     'under the cover' (but see next item).

  þ  C-language uses by default a different way of parameter passing than
     BASIC, PASCAL and some other languages.  But MicroSoft QuickBASIC
     compiler 4.5 allows the C-language convention to be used, and the
     M„rklin-driver for QuickBASIC expects this convention to be used.  This
     is reflected in the function specifications in MKLAPI.INC.  If you use
     the MKLAPI.INC file (strongly recommended!), then you won't have to
     worry about these conventions.



  ERRORS AND SIGNALS

  The driver is designed not to disturb your screen with error-messages.
| Therefore audiable signals are used to indicate unexpected problems.

| The OS/2 and DOS-drivers produce the same warning-signals:

| very high pitch, short 3000 Hz, 20 msec: M„rklin-Interface  The driver is
|             in stop-state, but some routine tries to send commands, which
|             are discarded.

| medium high pitch, long 2000 Hz, 300 msec: M„rklin-Interface seems to be
|             long-term blocked.  The transmit task could not deliver its
|             data.  Most likely the transmit buffer is full.  Check the
|             'stop'-light on the M„rklin Central Control if a stop-condition
|             is the cause (manually set, or electrical problem).

| high pitch, short 1000 Hz, 20 msec: A command-transmission did not finish
|             within the normal time.  Too many commands may be queued, maybe

  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                           Specifications  25


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
|             because of a program loop.

| medium pitch, short 440 Hz, 100 msec: Flushing of the buffer could not take
|             place in the expected time.  Either transmission of buffered
|             data doesn't take place, or the buffer is being filled during
|             flushing faster than can be transmitted.

| low pitch, short 200 Hz, 100 msec: a communications error occurred (OS/2).
|             Debugging information might be sent to STDERR (which you might
|             have redirected to a log-file to prevent disturbance of your
|             screen).













































  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                           Specifications  26


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  INSTALLATION



  APPLICATION DEVELOPMENT CONSIDERATIONS

  This MKLAPI is a program development tool with a C-language or QuickBASIC
  compiler.  You need MKLAPI.H (MKLAPI.INC for BASIC) at compile-time and one
  of the .OBJ files at LINK-time.  It is an addition to the compiler and
  possibly other toolkits you may have for other purposes.


  C-COMPILER CONSIDERATIONS

  The following compiler properties apply.

  þ  The file MKLAPI.H must be #included in the program that references the
     driver routines (you can use the same header-file for OS/2 and DOS).

  þ  Memory model: OS/2: LARGE; DOS: SMALL or LARGE (your choice)

  þ  Calling conventions: C

  þ  OS/2:  The '/MT' parameter should be specified with MicroSoft C-compiler
     6.00a  With IBM C SET/2 compiler '/Gm' should be specified among other
     parameters.

  þ  Generate underbars: On (Turbo-C option).

  Other compiler options are (probably) not of influence on the use of the
  M„rklin-driver.


  MICROSOFT QUICKBASIC COMPILER 4.5 CONSIDERATIONS

  The QuickBASIC compiler is needed to create an object deck of your BASIC
  program.  This OBJect file is combined with LMKLAPI.OBJ file as provided by
  this MKLAPI package to build an EXE-file with the LINK utility.

  þ  Calling conventions: C (DECLARE SUB|FUNCTION xxx CDECL ... etc)



  BUILDING AN EXE-FILE

  One of the OBJect files should be included in the link-step with your own
  OBJect file(s).  I prefer to Compile and LINK with the help of the (N)MAKE
  utility.








  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                             Installation  27


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  C-LANGUAGE AND DOS

  For the DOS sample application ("TRAIN") I use the following MAKE-file:

  ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
  ³                                                                         ³
  ³ #                                                                       ³
  ³ # MAKE TRAIN: Marklin Digital Train Control program (DOS version)       ³
  ³ #             - both SMARKLIN.OBJ and LMARKLIN.OBJ generated            ³
  ³ #             - LARGE memory model version used for TRAIN.EXE           ³
  ³ #             - With the compiler variable __DOS__ specified, certain   ³
  ³ #               #include-file selections are made in train2.c. When     ³
  ³ #               __DOS__ not specified the OS/2-inlcudes are selected.   ³
  ³ #                                                                       ³
  ³                                                                         ³
  ³ MDL=L                                                                   ³
  ³ CL=-c -Zl -Zp -G0 -W3 -A$(MDL) -D__DOS__ -Fotrain.obj -Ot               ³
  ³ LK=/NOD /PACKC:65500 /ST:4000                                           ³
  ³                                                                         ³
  ³ train.exe: train.obj smklapi.obj lmklapi.obj                            ³
  ³   LINK  train+$(MDL)mklapi, train $(LK), nul, $(MDL)LIBCER;             ³
  ³                                                                         ³
  ³ train.obj: train2.c train.h train.mak attrib.h attrib2.h common.h\      ³
  ³            matrix.h mklapi.h                                            ³
  ³   CL $(CL) train2.c                                                     ³
  ³                                                                         ³
  ³ smklapi.obj: mklapi.asm mklapi.h train.mak                              ³
  ³   MASM -Dsmall mklapi.asm,smklapi;                                      ³
  ³                                                                         ³
  ³ lmklapi.obj: mklapi.asm mklapi.h train.mak                              ³
  ³   MASM -Dlarge mklapi.asm,lmklapi;                                      ³
  ³                                                                         ³
  ³                                                                         ³
  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

  Note: It contains switches to control the use of large or small memory
  models.


  C-LANGUAGE AND BASIC

  For a simple test-program in QuickBASIC I use the following batch-file:

  ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
  ³                                                                         ³
  ³ @echo off                                                               ³
  ³ rem                                                                     ³
  ³ rem Build Marklin Digital Test program for DOS QuickBASIC               ³
  ³ rem Note: LMKLAPI.OBJ fetched from \C2\MARKLIN subdirectory             ³
  ³ rem                                                                     ³
  ³ BC    test /S;                                                          ³
  ³ if errorlevel 0  LINK  test+\c2\marklin\lmklapi;                        ³
  ³                                                                         ³
  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ


  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                             Installation  28


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  Note: With MicroSoft QuickBASIC compiler 4.5 the LMKLAPI.OBJ need to be
  included in the link.  models.


  C-LANGUAGE AND OS2 1.3

  For the 16-bits OS/2-sample application ("TRAIN2") I use the following
  MAKE-file for MicroSoft C-compiler 6.00a and IBM OS/2 Program Development
  Toolkit 1.2/1.3:

  ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
  ³                                                                         ³
  ³ #                                                                       ³
  ³ # MAKE TREIN: Marklin Digital Train Control                             ³
  ³ #                                                                       ³
  ³ # To be used with MicroSoft C-compiler 6.00a                            ³
  ³ #                                                                       ³
  ³ # With IBM C/2 1.1 compiler specify '__IBMC2__' compiler option         ³
  ³ #                                                                       ³
  ³ # 'OS2' compiler variable needed for OS/2 object of TRAIN2!             ³
  ³ #                                                                       ³
  ³                                                                         ³
  ³ CL=-c -Zp -Zl -W3 -MT                                                   ³
  ³ LK=/A:16 /PACKC:65000 /NOI /NOD                                         ³
  ³ L1=LLIBCMT OS2                                                          ³
  ³                                                                         ³
  ³ train2.exe: train2.obj mklapi2.obj train2.def                           ³
  ³    LINK train2+mklapi2, $@ $(LK), NUL, $(L1), train2.def                ³
  ³                                                                         ³
  ³ train2.obj: train2.c train2.h attrib2.h mklapi.h common.h matrix.h      ³
  ³    CL $(CL) train2.c                                                    ³
  ³                                                                         ³
  ³ mklapi2.obj: mklapi2.c                                                  ³
  ³    CL $(CL) mklapi2.c                                                   ³
  ³                                                                         ³
  ³                                                                         ³
  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

  The contents of the corresponding LINK .DEF-file are:

  ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
  ³                                                                         ³
  ³ ;                                                                       ³
  ³ ;******* Marklin Train Control Program  Definition File (.DEF) ******** ³
  ³ ;        For: 1)  16-bit version for OS/2 1.3 and MS C-compiler         ³
  ³ ;             2)  32-bit version for OS/2 2.0 and IBM C Set/2 compiler  ³
  ³                                                                         ³
  ³ NAME    TRAIN2  WINDOWCOMPAT                                            ³
  ³                                                                         ³
  ³ DESCRIPTION 'Marklin Train Control. Copyright (1991,93) Rob Hamerling'  ³
  ³ PROTMODE                                                                ³
  ³ HEAPSIZE   4096                                                         ³
  ³ STACKSIZE  8192                                                         ³
  ³                                                                         ³
  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                             Installation  29


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  C-LANGUAGE AND OS2 2.0+

  For the 32-bits OS/2-sample application ("TRAIN3"), the following MAKE-file
  is appropriate for IBM C SET/2 compiler and IBM OS/2 Program Development
  Toolkit 2.0:

  ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
  ³                                                                         ³
  ³ #                                                                       ³
  ³ # MAKE TREIN: Marklin Digital Train Control program                     ³
  ³ #                                                                       ³
  ³                                                                         ³
  ³ CL=/c /G3 /Gd+ /Gm+ /Re /Se /Sm /Ss                                     ³
  ³ LK=/NOI /PACKC:65500 /ALIGN:4 /BASE:0x10000 /EXEPACK                    ³
  ³                                                                         ³
  ³ train3.exe: train3.obj mklapi3.obj                                      ³
  ³    link386 $**, $@ $(LK), NUL, , train2.def                             ³
  ³                                                                         ³
  ³ train3.obj: train2.c                                                    ³
  ³    icc $(CL) /Fotrain3.obj train2.c                                     ³
  ³                                                                         ³
  ³ mklapi3.obj: mklapi2.c mklapi.h                                         ³
  ³    icc $(CL) /Fomklapi3.obj mklapi2.c                                   ³
  ³                                                                         ³
  ³                                                                         ³
  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

  Note: The same .DEF-file is used as for the 16-bit version.


  STORAGE AND PERFORMANCE

  There is yet not much to say about storage and performance of the driver.
  It is highly optimised code, and probably only a minor part of the 'real'
  railroad control program.


  MEMORY UTILISATION

  It is difficult to say how many storage is occupied by the OS/2-version of
  the M„rklin-driver.

  The DOS-version requires about 4K bytes of storage.


  PROCESSOR UTILISATION

  You might be curious about the cycles that will be consumed by the polling
  task.  I've done some measurements under OS/2 version 1.3 with the sample
  program TRAIN2.  On an 8 Mhz AT (80286) the polling takes between 10% and
  12% of the processor time (difference in processor utilisation between
  polling ON and OFF).  This number is practically independent of the number
  of M„rklin S88 encoder's that are specified for polling, but the polling
  frequency is also lower!


  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                             Installation  30


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  COMMENTS, REMARKS, BUG-REPORTS

  If there are bugs, requirements or questions about this M„rklin-driver, the
  documentation or the sample program (that you get when you register),
  please send me a message through the FIDO network.  You can find my name
  and node-(point)-number in the introduction of this document.

  Enjoy and good luck with your program development!  May this driver lead to
  a very attractive and succesful model railroad control program!

  Do not 'forget' to register!













































  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                             Installation  31


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  APPENDIX A.  MKLAPI INTERNALS

  This appendix describes a number of design arguments for this driver and
  explains decisions where a choice had to be made.


  MULTITASKING

  There are many situations in real-time programming, where you want the
  system to do something for you, while in the meantime you would like to do
  something else in the mainline (before the first piece of program
  completes).

  An example of this is reading sensor boxes.  While you have to wait for the
  response of the M„rklin S88 encoder, you might want to update your screen,
  read data from disk, or process keyboard input.  In many sample programs
  that I have seen, the wait is frequently done in the form of a short loop
  (a for- or while-statement).  This means that the processor is working, in
  fact consuming cycles, while you cannot do anything (unless you make a more
  'complicated' loop).  And in many cases you have to experiment with this
  loop to get the needed wait-interval (not too long and not too short).
  Running the same program on a machine with a different processor-speed,
  requires a change in the loop.

  A solution for this is to have multiple programs to run simultaneously.
  Executing multiple programs (tasks) in parallel is called multi-tasking.
  Since we are generally dealing with a single micro processor, the tasks are
  simultaneaously present in memory, but only 1 of them is actually
  processing.  There must be some mechanism to switch the processor between
  the tasks.

  Some operating environments have standard facilities for this (OS/2,
  Windows), but DOS doesn't.  Under DOS you have to do it yourself.  By
  intercepting hardware interupts, or the timer-tick interrupt it is possible
  to implement a kind of task-switching.

  The polling mechanism in the M„rklin-driver is a form of multi-tasking.
  For OS/2 it uses the standard OS/2 facilities (called multi-threading), for
  DOS it uses the system timer to execute periodical actions independently
  from the main-program, and also the hardware interrupts of the asynchronous
  communications port to perform some communications work.  So in fact there
  are two 'extra' tasks in the polling mechanism:

  þ  Periodically send read-commands to the M„rklin-Interface.
  þ  Receive the responses and put them in the appropriate place in the
     sensor-array.

  Although you don't have to bother about the polling mechanism, it does have
  some influence on the design of your railroad control program.  These
  practical aspects are explained below.






  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                            Appendix A.  MKLAPI Internals  32


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  READING M„RKLIN S88 ENCODERS

  The driver generates read-sensor commands in the following way:

  1. After polling is activated periodically a sensor-read command is
     transmitted to read multiple M„rklin S88 encoders.

  2. The receive-part of the communications task is signalled that a response
     from the M„rklin-Interface should be expected.  The receive continues as
     long as not all expected input is received, or an unexpected long time
     had to be waited.

  3. After processing the response, the system waits some time before issuing
     a new read command (typically 100 msec).

  4. Even if for some reason the previous poll did not finish within
     reasonable time (typically 500 msec), a new read-command is issued.

  5. If the transmit routine is in use by the mainline program (such as
     sending train-commands), polling is suspended for a short while (shorter
     than the normal polling interval).

  The M„rklin-Interface documentation indicates that the average time to read
  the last poll-response is between 45 and 300 milliseconds, depending on how
  many M„rklin S88 encoder's are being read.  From 'life'-tests I have
  concluded:

  þ  The total polling cycle (the time between two consecutive read commands)
     is so short that the delay between the change of a switch and making the
     change represented in the sensor-array is short enough for most
     practical situation.
  þ  The poll wait interval is long enough to allow sending of many commands
     from the mainline between read commands.  To make this sure there is a
     built-in priority mechanism in the polling routine: it waits with
     generating a poll when another program uses mklputc() routine!
  þ  The frequency of the polls is low enough to ensure that not all CPU
     cycles are spent on polling, in stead of 'real' work.

  Polling is programmed as follows:

  1. After calling mklpoll() of mklgo() with a non-zero parametervalue a
     '192'-byte is transmitted, meaning that the Interface will RESET the
     bits with next read-sensor commands.
  2. Periodically a '128 + MAXSENSOR' byte, meaning that the Interface will
     report a group of sensors, up till the limit that was specified with the
     latest mklpoll() or mklgo().


| The received data is collected in 2 sensor-arrays:

| 1. Collection of 'raw' data from the M„rklin-Interface.  Array-1 always
|    represents the current switch positions of all polled S88's, apart from
|    a slight delay between consecutive reads.



  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                            Appendix A.  MKLAPI Internals  33


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  

|                    ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
|                    º                   º
|                    º Marklin Interface º
|                    º                   º
|                    ÈÍÍÍÍÍÍÍ-ÍÍÍÍÍÍÍÍÍÍ¼
|                            º  º
|                            º  º
|     ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍºÍÍºÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
|     º    READ S88 1...6 ÍÍÍ¼  º                         Computer    º
|     º  (by polling task)      º                                     º
|     º                         º                                     º
|     º                         º                                     º
|     º          ÉÍÍÍÍÍËÍÍÍÍÍËÍÍÊÍÍËÍÍÍÍÍËÍÍÍÍÍ»                      º
|     º  'move'  º     º     º     º     º     º                      º
|     º          º     º     º     º     º     º                      º
|     º       ÉÍÍÍÍËÍÍÍÍËÍÍÍÍËÍÍÍÍËÍÍÍÍËÍÍÍÍËÍÍ Í               º
|     º       º  1  º  2  º  3  º  4  º  5  º  6  º        array-1    º
|     º       ÈÍÍËÍÍÊÍÍËÍÍÊÍÍËËÍÊÍÍËÍÍÊÍÍËÍÍÊÍÍËÍÍÊÍÍ Í               º
|     º                       º                                       º
|     º   'or'   º     º     ºº(2) º     º     º                      º
|     º                       º                                       º
|     º       ÉÍÍÍÍËÍÍÍÍËÍÍÍËÍÍÍÍËÍÍÍÍËÍÍÍÍËÍÍ Í               º
|     º       º  1  º  2  º  3  º  4  º  5  º  6  º        array-2    º
|     º       ÈÍÍÍÍÍÊÍÍÍÍÍÊÍÍËÍÍÊÍÍÍÍÍÊÍÍÍÍÍÊÍÍÍÍÍÊÍÍ Í               º
|     º                      º                                        º
|     º                      º(1)   actions by: mklgetsn(3)           º
|     º                      º     1. return word 3 of array-2        º
|     º                           2. copy word 3 array-1 to array-2  º
|     º                                                               º
|     ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


| Figure 1. Organisation of reading S88's (polling): In this sample a
|           group-read of 6 S88-boxes is used.

| 2. Cumulative 'on'-bits since most recent mklgetsn() for each specific S88
|    in Array-2.

| The incoming data of the 'read group' is stored in array-1, and all 1-bits
| are copied immediately to array 2 with an 'or'-operation.  So array-2 is a
| cumulation of 'on' switch positions during a certain period.

| When mklgetsn(x) is executed, the contents of word-x in array-2 are
| returned to the caller.  At the same time word-x in array-2 is refreshed
| with the then current contents of array-1.  So a second mklgetsn()
| immediately after the first gives the actual status ((3)).
| A second call is required if you want to know for sure if the switch is
| currently in the 'off'-position after it has been 'on' since the most
| recent mklgetsn().

  
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  (3)     Function mklgetsn might be changed later to be able to specify that
          you need data from the first or from the second array.

  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                            Appendix A.  MKLAPI Internals  34


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
| This mechanism is suitable for all types of switches that are applied in
| model-railroads, and ensures that you won't miss any 'switch-on' condition,
| even if it is 'on' during a very short period.  This organisation is
| illustrated in Reading M„rklin S88 encoders  on page 33.

  You have to be careful with specifying more M„rklin S88 encoder boxes in
  mklpoll() or mklgo() than you really have in your model railroad yard.

  þ  It is not useful, since the M„rklin-Interface will return all zeroes for
     not-connected M„rklin S88 encoder's.
  þ  During the time the M„rklin-Interface sends the responses to the
     computer, no commands are accepted by the Interface.

  So specifying more M„rklin S88 encoders than really active will unnecessary
  downgrade the responsiveness of your program.  You might decide to stop
| polling during processor-intensive work, or not to use polling at all.

| Note: The following consequences of this mechanism:

| þ  If you use this driver, you should not issue read-commands from the
|    mainline.  The driver does not intercept read-commands from the
|    mainline, but it will intercept all data from the Interface and not
|    return it to the mainline!  This will disturb the administration of the
|    internal sensor numbering, which is depending entirely on the number of
|    incoming bytes.
| þ  This driver does not yet support physically reading of individual
|    M„rklin S88 encoders, and it is not possible to use polling with
|    no-reset (command 128 in stead of 192).  This may look like a
|    limitation, especially with the use of reed-switches or contact-rails.
|    But once you are familiar with the convenience of the polling mechanism
|    and the functionality of mklgetsn(), this should not be a practical
|    limitation.



  COMMUNICATIONS INTERFACE SPECIFICATION

  The M„rklin-Interface contains a device driver level communication facility
  with between computer and M„rklin-Interface, but with a rather high level
  interface for the application programmer.  It contains many basic
  functions, that otherwise have to be programmed yourself.  However, it
  enforces a specific organisation of your program and has some limitations.

  Some of the internals of the communications task are briefly explained to
  show why it works as it works now, and may prevent questions.  On the other
  hand, it may trigger suggestions for changes!  Feel free to go in
  discussion with me!

  Wiring          Only the Read (RD), write (TD) and Clear-to-Send (CTS) lead
                  are connected.  Thus using DTR and RTS from the computer
                  will have no effect of any kind and obviously DSR and DCD
                  (sometimes also called CD or RLSD) will not be used by the
                  M„rklin-Interface  Nevertheless DTR and RTS are set by the
                  driver with mklopen().  This allows for the use of a
                  break-out box and/or another computer in stead of the

  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                            Appendix A.  MKLAPI Internals  35


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
                  M„rklin-Interface for debugging of your program (since a PC
                  commmunications program usually needs these leads to be
                  active).  The driver itself works properly without the DSR
                  and DCD leads.

  Speed           The M„rklin-Interface allows only 2400 bps, and 8-bits
                  data, NO parity, and 2 stop bits.  These are the built-in
                  defaults of the driver, however a different speed can be
                  specified at open-time (might be useful for test and
                  debugging).

  FIFO            So called FIFO hardware buffering, provided by the newer
                  UART-chips (such as 16550 AFN) on asynchronous
                  communication ports is handled as follows by the drivers:
                  þ  The DOS-driver does not actively support FIFO-mode, but
                     FIFO-support is in plan.
                  þ  The OS/2-MKLAPI uses the facilities of the device driver
                     COM[xx].SYS for operation of the COM-port.  When FIFO is
                     is active for the COM-port before opening, it is left
                     active and uses this feature.  Use the MODE-command to
                     control this feature.

                  FIFO-mode may not provide a considerable improvement:
                  þ  The M„rklin-Interface operates strictly half-duplex, it
                     is either in receive mode, or in transmit mode.  During
                     data transfer (either way) CTS is dropped while
                     transmitting each command-byte and may remain low for a
                     'considerable' time while command interpretation is in
                     progress and S88-positions are being sent back to the
                     computer.  This does not suit very well with the FIFO
                     for transmitbuffering.  It might be useful for receive,
                     since in many cases at least 2 bytes are received per
                     S88. being read.  The support for this is in
                     consideration.
                  þ  Since the speed is 2400 bps, most systems can easily
                     keep up with the non-buffered mode of operation.  The
                     highly effective interrupt handler of the DOS-driver may
                     make the netto effect of reduced CPU-cycles for
                     interrupt handling only minimal.

                  But FIFO-mode may be helpful in a multitasking environment.
                  Use the MODE command with BUFFER=ON, to activate it, when
                  desired.

  Output flow control The CTS signal is dropped by M„rklin-Interface during
                  data transfer (during receive and transmit: the
                  M„rklin-Interface is strictly half-duplex).  The CTS signal
                  is used for 'hardware output flow control' from the
                  computer.  So the transmit routines will not send data when
                  CTS is not high, but will automatically resume transmission
                  when CTS rises and the buffer contains any data to
                  transmit.

                  DOS Although not strictly needed, the DOS-version of the
                  M„rklin-driver has the transmit interrupt (THRE) active to

  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                            Appendix A.  MKLAPI Internals  36


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
                  be able to run the driver against a full-duplex interface
                  (with continuous CTS), such as another PC with a diagnostic
                  communications program.  The transmit interrupt uses the
                  same code as the MSR interrupt.

                  For initial testing of programs without actually running a
                  model railroad, you could use a 'wrap-plug' to partially
                  simulate the M„rklin-Interface.  The RTS signal (raised by
                  the driver) is feeded back to CTS, so the driver is always
                  able transmit.

                  If also send and receive (generally pins 2 and 3) leads are
                  wrapped back, then the transmitted data is treated as S88
                  response.  This may cause

  Input flow control There is no form of input flow control allowed by the
                  M„rklin-Interface: there is no way to signal the
                  M„rklin-Interface to stop sending.  This will not be a
                  problem for the driver, since there is enough buffering and
                  CPU-power to process the low volume input in time.

  XON/XOFF flow control Not used.  This type of flow-control is not supported
                  by the M„rklin-Interface, since the commands for the
                  M„rklin-Interface may contain these characters!

                  OS/2: The standard COM[xx].SYS of OS/2 allows simulated
                  XON/XOFF.  A DosDevIOCtl-'XOFF' is issued to stop
                  transmitting buffered data when a 'stop'-command has to be
                  transmitted.  A DosDevIOCtl-'XON' is issued when a
                  subsequent 'go'-command is issued.

  Null stripping  The OS/2 COM[xx].SYS allows null stripping.  There are at
                  least 2 reasons for this feature not to be activated:
                  þ  M„rklin S88 encoder's may respond with all bits zero
                  þ  Switch 256 is addressed as ASCII 0.

  Command parsing The driver does not interpret the data it sends to the
                  M„rklin-Interface.  It means that it is completely the
                  responsibility of the mainline to ensure proper command
                  sequences.

                  Note: The driver does not send automatically a
                  switch-'relax' command (ASCII 32) after a switch command
                  (ASCII 33 or 34)!  You may write a shell for M„rklin
                  command syntax checking.



  PROBLEMS WITH OS/2 COM[XX].SYS

  The Com-port driver of some versions of OS/2 for non-PS/2 machines
  (COM01.SYS) does have some known problems, such as:

  þ  READ and WRITE timout specifications cannot be changed from the built-in
     default of 1 minute.

  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                            Appendix A.  MKLAPI Internals  37


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  When encountering this kind of problems, I could recommend Gerry Rozema's
  replacement driver for AT-type machines (COM16540.SYS, or COM16550.SYS, as
  appropriate for your system's COM-port).  For OS/2 2.0 there is also a
  driver SIO.SYS by Ray Gwinn, that might be useful when having problems with
  the standard OS/2 2.0 drivers.

  These alternative drivers are available on Bulletin Boards such as
  PC-Square in The Netherlands (FIDO node 2:512/4, telephone 31.79.424107).


  OS/2 AND DOS DIFFERENCES

  Although all versions of this M„rklin-driver offer a consistent application
  programming interface for communication with the M„rklin-Interface, it is
  most likely that there will be differences between the programs using
  either of them.  Some of these differences might be:

  þ  When running in a multitasking environment, the program should give
     other tasks the chance to run (yield the processor).
     ù  With OS/2 other tasks will get some control automatically
        (pre-emptive multi-tasking), but nevertheless the program should at
        least use DosSleep(0) when it does not need the processor for some
        time.
     ù  DOS: apart from the built-in multitasking of the M„rklin-driver which
        controls itself, you probably won't run other programs.  In that case
        you will not have to release the processor.
     ù  When running a DOS-program under another multitasker (Windows,
        Desqview), periodic calls of mklsleep() are recommended.

  þ  The OS/2 driver makes use of the standard multitasking (multithreading)
     facilities.  Therefore any program using this driver should specify /MT
     for MicroSoft C-compiler 6.00a.  The different include-search might be
     indicated with a compiler option (-I for most C-compilers).

     The DOS driver should use the normal include directory.

  þ  The OS/2 driver requires the LARGE memory model compiler options and use
     the LLIBCMT library for LINK (automatic with /MT).  The DOS-version is
     for either the SMALL (/AS) or LARGE memory model (/AL), use the
     respectively the SLIBCE or LLIBCE library with LINK.

  þ  The standard OS/2-driver (COM[xx].SYS) will not accept new output data
     in stop-state, but will transmit possibly retained data (from before
     mklstop) after a call to 'mklgo'.  Some alternative drivers (such as
     SIO.COM) do accept new data from mklputc, but keep it internally
     buffered.  No more data is accepted when the buffer is full.  After
     mklgo() all buffered data, old and new, will be transmitted.

     The DOS-drivers refuse all new output data in stop-state.

  þ  It is an absolute must, that the M„rklin-driver under DOS is terminated
     with a call to mklclose() to de-activate the interrupts for com-port and
     timer.  Therefore it is recommended to use a routine to intercept Ctrl-C
     or Ctrl-Break actions from the keyboard.


  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                            Appendix A.  MKLAPI Internals  38


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
     Under OS/2 this attitude is recommended, but not an absolute must.

     In both cases it is recommended to direct the Ctrl-C signal to a
     controlled finish of your railroad control program: you probably do not
     want to terminate your program with uncontrolled running trains!

  þ  The display of information about the state of your railroad on the
     computer screen will probably use different techniques, such as the way
     cursor and color will be used:
     1. OS/2: Presentation Manager (graphics) or VIO routines.
     2. DOS: Windows (graphics)
     3. ANSI escape-sequences (compatible between OS/2 and DOS)

     The sample program you'll receive after registration is a single source
     for environments 1 and 3.  My own programs are primarily for OS/2 and I
     prefer to use the OS/2 facilities and those of the Program Development
     Toolkit as good as possible.  For instance I use VIO-routines for color
     and cursor manipulation.

     To be able to run my sample program under DOS, I included some extra
     routines in the header-file.  These routines translate color and cursor
     manipulations with OS/2 VIO-calls into equivalent ANSI escape sequences.
     When ANSI is active under DOS (with DEVICE=[path]\ANSI.SYS in
     CONFIG.SYS), the visual effects are the same as with the OS/2 version.

  When there is no possibility to use the same code for OS/2 and DOS, you
  might consider using a compiler variable (with the -D compiler option) to
  distinguish which pieces of codes are OS/2 or DOS specific.  See for an
  example the MAKE-files in the MKLAPI package.



























  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                            Appendix A.  MKLAPI Internals  39


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  APPENDIX B.  TRACE FACILITY



  TRACE RECORDS

  The trace facility produces the following records (8 bytes each):


   long int timestamp;  /* value of mkltime */
   int  fl:1,           /* flag: 0=output, 1=input */
        nn:7,           /* (in start-of-trace record) trace source */
                        /* MKLAPI: DOS = 1; OS/2 1.x = 2; OS/2 2.x = 3 */
        sw:8;           /* S88 box number on input */
   char c1,             /* first character */
        c2;             /* second character */

  The first record after starting a trace contains 0xFF as first and second
  character.


  SAMPLE

  The output of the trace formatting program MKLTRFMT will look like:


        time    I/O  cmd  data  description
   ------------ ---  ---  ----  --------------------------------------
         45.050                 Start of trace (MKLAPI OS/2 1.x)
         +0.045  O    1A    13  Loc 19  speed 10  Funktion=ON
         +0.350  O    22    3F  switchpoint 63: branch
         +0.760  O    20        switchpoint release
         +1.850  O    C0        read S88's with reset
         +4.850  O    82        read S88 1 t/m 2
         +4.881  I        1801  S88  1 ON=4,5,16
         +4.881  I        090E  S88  2 ON=,8,13,14,15
         +5.000  O    61        STOP

  This is not a complete trace, just some parts to show the essentials.

  MKLTRFMT.EXE is a 'family mode' application: it will run under OS/2 and
  DOS.  No parameters are required, but you may specify the input filename
  [including path] if your trace is in another directory or named other than
  MKLAPI.TRC, which is the default (output filename of MKLAPI).

  MKLTRFMT writes the output to 'stdout', which is normally the computer
  display.  But the output may be redirected to your printer or to a file.
  So you could use for example the command:

    MKLTRFMT >TRACE.FMT

  so that you could look afterwards with a text editor or file browse utility
| in TRACE.FMT for the formatted trace.



  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                              Appendix B.  Trace facility  40


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
| APPENDIX C.  M„RKLIN-INTERFACE PECULIARITIES

| When writing a model railroad control program (with or without this
| driver), you should be aware of some peculiarities, which are not very well
| (or not at all) documented by M„rklin.  With experiments during development
| of MKLAPI I have found for example:

| þ  Sending 2 consecutive change-direction commands to the same loc does not
|    put the loc back in the original direction.  A zero-speed command
|    between them is a good circumvention.

| þ  When the M„rklin-Interface is in 'stop'-state:
|    ù  Permanent blocking (having to push the 'go'-button on the M„rklin
|       Central Control)  does occur only with commands to train-decoders and
|       switch-point or light decoders (K83 or K84).
|    ù  Reading M„rklin S88 encoders (polling) may continue.  But since the
|       changes are not sent from the control-box to the M„rklin-Interface,
|       it is not very useful.






































  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                             Appendix C.  M„rklin-Interface peculiarities  41


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
  APPENDIX D.  SUMMARY OF CHANGES

  0.7   First beta release: June 1992

  0.8   released: October 1992
        þ  The time-base value in mkltime has been changed from 55 msec to 1
           msec!(updating of mkltime still on timer-tick basis: once per 55
           msecs in DOS, once per 31.25 msecs in OS/2).
        þ  DOS: High precision timer routine added: mklmsecs().  This gives
           the period since line to opening of communication with
           M„rklin-Interface  with 1 msec accuracy.
        þ  OS/2: Trace facility added (see also "Appendix B.  Trace facility"
           on page 40), start and stop of trace via procedure call
           mkltrace().  Output to and input from the M„rklin-Interface is
           traced.  A trace-file formatting utility (MKLTRFMT.EXE) is added
           to package.  I have tried to add this trace facility also in the
           DOS driver, but I did not cucceed so far.  It is rather
           complicated to use DOS facilities during interrupt handling
           (tracing must be located in the com-port and timer interrupt
           routines).
        þ  A procedure 'mklsleep' added to make your DOS-program 'friendly'
           for some popular multitasking environments (such DOS-box of OS/2,
           Desqview, Windows).
        þ  DOS: mklflush times out after 3 seconds when transmit buffer could
           not be flushed.
        þ  Some bugs fixed:
           ù  mklflush() of OS/2 version watched the INput in stead of OUTput
              queue.
           ù  DOS: DTR and RTS now turned off before finishing program.

  0.9   released: March 1993
        þ  A 32-bits driver for OS/2 2.0+ (MKLAPI3.OBJ) has been added, with
           same functionality as MKLAPI2, including the new features below!
        þ  'MKLAPI' now also useable by programs translated with the
           MicroSoft QuickBASIC compiler 4.5.  Since QuickBASIC does not
           allow underscores in names, all externally used names have been
           changed, for example: mklopen() is now called mklopen().  The
           C-language calling convention must be specified in the source (see
           MKLAPI.INC), and the file LMKLAPI.OBJ should be used with LINK.
           All function specifications have been changed, and additions made
           for program development with MicroSoft QuickBASIC compiler 4.5.
        þ  mkltime() is not anymore an external variable, but a function
           returning the value of the time, expressed in milliseconds, but
           with the precision of the timer tick.
        þ  mklmsecs() now also a function returning the time, but in exact
           milliseconds (DOS only).
        þ  With the OS/2 drivers, the transmissions in STOP-state (after
           mklstop) may now be buffered in stead of discarded (until buffer
           full, then discarded).  This depends on the COM.SYS device
           drivers, or replacements thereof.
        þ  After the first mklstop subsequent calls of mklstop are ignored
           and nothing sent to the M„rklin-Interface until mklgo has been
           called.
        þ  mklstop() and mklgo() now give a returncode (0 = OK, otherwise a
           transmission problem exists).

  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                          Appendix D.  Summary of changes  42


  MKLAPI
  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  
  
        þ  Simple Switchpoint test program (incl c-source) added to MKLAPI
           package.
        þ  Added counters for and a function mklstats() for statistical
           purposes and debugging.
        þ  Polling optimised: a single 'reset after read S88' (192) is issued
           after mklpoll() and mklgo(), subsequently only 'read group of n
           S88s' (128+n) commands are sent periodically (previously both
           commands were sent after each interval).

  1.0   released: May 1993
        þ  Names and references to 'MARKLIN' renamed to MKLAPI, where the
           driver is meant (and not M„rklin-components).  Include-files and
           sources that include header files should be changed.
        þ  DOS-drivers now take RS232 port addresses from the BIOS data-area,
           and performs a simple check if the port is not already in use.
        þ  Sound support added to DOS-drivers, and the function made callable
           by mainline.  Warning signals of OS/2- and DOS-drivers
           'harmonised'.
        þ  Polling and storage of S88 bit-settings changed to get better
           operation for all types of switches.
        þ  mklstop() and mklgo() made more reliable.
        þ  mklsleep() accepts now specification of an interval (pause) time
        þ  mklmsecs(), mklsound() and mklsleep() functions now present in
           both OS/2 and DOS versions for more compatibility between OS/2 and
           DOS versions of programs that make use of the MKLAPI-driver.































  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                          Appendix D.  Summary of changes  43