PortaCall(c)


If you regularly use your cellular phone to check your answering
machine messages, then PortaCall is the program for you.

With PortaCall, your computer will call you whenever a new message is
on your machine.  PortaCall lets you know there is a message, by
dialing your cellular phone, leaving a few harmless rings and then
hanging up.

When you hear the rings you can then dial up your answering machine and
retrieve your new message.

PortaCall will make you more responsive to your customers and will save
you money in cellular phone charges-  You'll only call your answering
machine when you KNOW there are messages.



                     Hardware Requirements and Setup


To use PortaCall you'll need an answering machine and a Hayes
compatible, auto-dial modem.  PortaCall will dial out on either
a PULSE or TONE phone system.  The default setting is TONE,  if you
want PULSE you must put a 'P' before the phone number (see examples
below).

The proper setup for the answering machine and modem should be:

        -   Connect the modem LINE jack to the answering machine PHONE
            jack.

        -   Connect the answering machine LINE jack to the wall jack

You may require a different configuration if you have additional phone
equipment, such as a fax machine, to consider.  The bottom line is, you
want the answering machine and the modem to sense incoming calls at the
same time.

When properly connected your answering machine should pick up calls as
usual and (without any communications software running) your modem
lights should blink whenever you receive phone calls.  If you have an
internal modem, obviously, you cannot check the lights.  In this case
just make sure the answering machine is working properly.














                                (1)

                           Running the Program


1.      Before you leave your office, turn on your PC and modem

2.      Load PortaCall by entering:

             PCALL [cellular phone#] [wait time]  [ring count]

        For example:

             PCALL 555-1212 2 3
        or

             PCALL P555-1212 2 3       (this option uses PULSE dialing).


Will set PCALL to dial 555-1212 two minutes after your answering
machine receives a message.  PortaCall will leave three rings on the
cellular phone and then hang up.



                           Things to Consider

The WAIT TIME is in minutes.  It begins as soon as your office phone
rings. You should use a WAIT TIME that is long enough for someone to
leave a nice long message.  If the wait time is too short, then
PortaCall may begin dialing your cellular phone before the caller
finishes his message.

The RING COUNT is based on the standard '6 seconds per ring' timing on
most phones.  On cellular phones there is sometimes a long delay before
the first ring occurs.  It may be best to add 1 to the ring count.  For
example, if you want PortaCall to leave 2 rings on your cellular phone,
use 3 as the ring count.


                         Checking Your Messages

Whenever your cellular phone rings a few times and then stops, you'll
know there are messages waiting for you. In the mean time, PortaCall
will have looped back to wait for the next phone call to your answering
machine. When you call up to get your messages you will be activating
PortaCall again. Because PortaCall doesn't know that it's you checking
your messages, it will, again, call your cellular phone a few minutes
after you've dialed in. If you are certain that this second PortaCall
call is due to your message checking, then just ignore it.











                                (2)




                          The PortaCall Screen

The PortaCall screen shows the values you chose when you started
PortaCall.  To modify these values, press ESC to exit PortaCall and
then start the program again with new values:

          Dial      Indicates the cellular phone number

          Wait      Indicates the delay time between when a message is
                    left on the answering machine and when PortaCall
                    dials the cellular phone

          Rings     Indicates the number of rings to be left on the
                    cellular phone

          Status    Indicates the status of PortaCall

The last line on the PortaCall screen shows the status of PortaCall. 
The different status' and their meanings are as follows:


     Waiting for a Phone Call      PortaCall is listening to your
                                   modem to see if it rings.       
                                   

     nnn Seconds Until Dial        PortaCall has sensed a ring on the 
                                   modem and is counting down before it
                                   dials your cellular phone.

     Dialing                       PortaCall is dialing your number


     Not Enough Info to Load       You started PortaCall and either the
                                   phone number, the wait time or the
                                   ring count were missing.

     Phone Number is too long      The phone number can be 15
                                   characters

     Wait time is not valid        The wait time must be between 1 and
                                   9

     Ring Count is not valid       The ring count must be between 1 and
                                   9








                                (3)



                              Registration

It would be greatly appreciated if you registered PortaCall with its
author.  PortaCall should save you a great deal of time and money if
you use it regularly.  For this I ask just $10.00.

Please register by sending a check or money order for $10.00 to Bill
Dineen, 455 Hope Street #3F, Stamford, CT  06906.

If you have any questions about PortaCall, my CIS ID# is 76370,2451.


                                (4)