ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
    ³                                                                       ³
    ³ ±±±ÜÜ±±±Ü ±±±±±±Ü ±±Ü ±±Ü    A QWK-compatible mail door for RBBS-PC   ³
    ³ ±±Û±±Û±±Û ±±Ûß±±Û ±±Û ±±Û   Copyright (C) 1991-93 Newark Connections  ³ Û
    ³ ±±Û ßß±±Û ±±±±±±Û ±±Û ±±Û       Copyright (C) 1993 Makai Software     ³ Û
    ³ ±±Û   ±±Û ±±Ûß±±Û ±±Û ±±Û               All rights reserved           ³ Û
    ³ ±±Û   ±±Û ±±Û ±±Û ±±Û ±±±±±±Ü                                         ³ Û
    ³  ßß    ßß  ßß  ßß  ßß  ßßßßßß        Version 3.10, June 6, 1993       ³ Û
    ³                                                                       ³ Û
    ³           ±±±ÜÜ±±±Ü ±±±±±±Ü ±±±ÜÜ ±±Ü ±±±±±±Ü ±±±±±±Ü ±±±±±±Ü ±±±±±±Ü ³ Û
    ³           ±±Û±±Û±±Û ±±Ûß±±Û ±±Û±±Û±±Û ±±Ûß±±Û ±±Ûßßßß ±±Ûßßßß ±±Ûß±±Û ³ Û
    ³           ±±Û ßß±±Û ±±±±±±Û ±±Û ß±±±Û ±±±±±±Û ±±Û±±±Ü ±±±±±Ü  ±±±±±Ûß ³ Û
    ³           ±±Û   ±±Û ±±Ûß±±Û ±±Û   ±±Û ±±Ûß±±Û ±±Û ±±Û ±±Ûßßß  ±±Ûß±±Ü ³ Û
    ³           ±±Û   ±±Û ±±Û ±±Û ±±Û   ±±Û ±±Û ±±Û ±±±±±±Û ±±±±±±Ü ±±Û ±±Û ³ Û
    ³            ßß    ßß  ßß  ßß  ßß    ßß  ßß  ßß  ßßßßßß  ßßßßßß  ßß  ßß ³ Û
    ³                                                                       ³ Û
    ³                              ±±±±±±Ü ±±Ü     ±±Ü ±±Ü ±±±±±±Ü          ³ Û
    ³                        ±±Ü   ±±Ûß±±Û ±±Û     ±±Û ±±Û ±±Ûßßßß   ±±Ü    ³ Û
    ³ Makai Software       ±±±±±±Ü ±±±±±±Û ±±Û     ±±Û ±±Û ±±±±±±Ü ±±±±±±Ü  ³ Û
    ³ 870 Golden Drive       ±±Ûßß ±±Ûßßßß ±±Û     ±±Û ±±Û  ßßß±±Û   ±±Ûßß  ³ Û
    ³ Newark, OH 43055        ßß   ±±Û     ±±±±±±Ü ±±±±±±Û ±±±±±±Û    ßß    ³ Û
    ³                               ßß      ßßßßßß  ßßßßßß  ßßßßßß          ³ Û
    ³                                                                       ³ Û
    ³ Support bulletin boards: (310)843-5732  (318)345-1955                 ³ Û
    ³                                                                       ³ Û
    ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ Û
      ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß
    
    
        "Go gently among the messages and comments that have been left and
        remember what peace there may be in silence."
    
        "...Be proud of those whose company you keep -- all those that are
        running or have ever run RBBS-PC."
    
        "...Be careful.  Strive to be happy and enjoy......."
    
                                                            Tom Mack
                                                            July 28, 1986
    


     TABLE OF CONTENTS                                               - Page i -
     

         GENERAL INFORMATION                                        1
             An Introduction to Mail Manager +Plus+                 1
             Warranty, Distribution, and Registration               2
             Registration Form                                      5
             Features and Limitations                               6
             Checklist of Requirements                              8
         
         INSTALLING MAIL MANAGER +PLUS+                             9
             ** Before you begin, READ THIS! **                     9
             Upgrading from a previous version                     10
                 From v1.3x                                        11
                 From v2.0x                                        11
                 From v3.0x                                        12
             Installing from scratch                               12
             Locked BPS rates                                      15
             Command line options                                  16
             Planning your user interface                          18
             Sysop-configurable text files                         21
             Text files for FIDO/netmail areas                     24
         
         CONFIGURING MAIL MANAGER +PLUS+ (MAILCFG.EXE)             26
             Screen #1 (General configuration #1)                  28
             Screen #2 (General configuration #2)                  32
             Screen #3 (Conference selection)                      37
             Screen #4 (Conference parameters)                     38
             Multiple configuration files                          45
         
         FIDO-STYLE *.MSG MESSAGE AREAS                            46
             An introduction to FIDO format                        46
             Setting up FIDO conferences                           47
             Netmail areas                                         50
             Netmail messages within reply packets                 53
             Additional thoughts                                   55
         
         MISCELLANEOUS CONSIDERATIONS                              56
             Debugging your setup and running in local mode        56
             Handling non-standard port addresses via MAILMGR.PRO  60
             DESQview, networks, and multiple nodes                62
             Using a FOSSIL                                        64
             QWK networking                                        65
             Compressing the executable files                      65
             Security features of Mail Manager +Plus+              66
             Additional features                                   68
         
         UTILITY PROGRAMS BUNDLED WITH MAIL MANAGER +PLUS+         71
             CFG2TXT & TXT2CFG - binary <-> text utilities         72
             MAILFIX, *M.DEF purge utility                         76
             MMINDEX, indexing utility for *.MSG areas             81
             MMGRNODE, node list compiler                          82
             MNET, QWK network QWK->REP conversion utility         83
             MUSER, editor for MAILMGR.USR user file               84
             UPDATE and UPDATUSR, upgrade utilities                86
         


    TABLE OF CONTENTS                                               - Page ii -
     

         MENU COMMANDS                                             87
             Main menu                                             87
                 C - Configure Mail Manager                        87
                 D - Download new mail                             87
                 E = Expedite!                                     88
                 G - Goodbye                                       88
                 Q - Quit                                          88
                 H (or ?) - Display help file                      88
                 I - Sysop information                             88
                 R - Read messages                                 89
                 P - Post a message                                89
                 U - Upload replies                                89
                 W - Who's online?                                 90
                 X - Expert toggle                                 90
             Configuration menu                                    91
                 A - Conference selection                          92
                 X - Message selection                             93
                 B - Q)WK or T)ext format                          93
                 C - Mark msgs addressed to ALL as personal        93
                 D - Extract personal mail ONLY                    94
                 E - Extract messages written by you               94
                 F - Abort packet if no new messages               94
                 G - Send updated bulletins                        94
                 H - Send new file listings                        94
                 I - Ask before sending packet                     94
                 J - File compression method                       94
                 K - File transfer protocol                        94
                 L - Update high message numbers after downloading 95
                 M - Update high message numbers after R)eading    95
                 T - Toggle 'turbokeys'                            95
                 ? - Display help file                             95
                 Q - Quit (finished configuring)                   95
         
         APPENDICES
             Appendix A: Common problems                           96
             Appendix B: Contacting the authors                    99
             Appendix C: Acknowledgements                         101
             Appendix D: File formats                             102
             Appendix E: About this document                      106


     MAIL MANAGER +PLUS+ GENERAL INFORMATION                         - Page 1 -
     

         INTRODUCTION
         ------------
         
         The 'QWK' format has been around for some time now, and is intended as
         a standardized way to transfer mail, news, and bulletins between your
         bulletin board and your users.
         
         Mail Manager was conceived as a way to handle RBBS-PC message bases
         offline, via this 'QWK' format used by popular mail readers such as
         SLMR, JABBER, OFFLINE, OLX, and many others.
         
         This type of mail transfer is normally a four-step process:
         
              1) The users call your BBS, open the QWK-style mail door, and
                 download their *.QWK mail packets.
              
              2) The users then log off the BBS, and use any number of QWK-
                 compatible offline mail readers to read and reply to messages
                 contained in the mail packets.  When they exit their mail
                 readers, any messages entered in that session are packed up
                 into what is termed as "reply packets".
              
              3) The users then call your BBS back up, open the QWK-style mail
                 door, and upload their reply packets (*.REP).
              
              4) The QWK-style mail door then processes the reply packet, and
                 inserts the new messages into the proper message base(s).
         
         Having experienced this marvelous system on other bbs types, we
         searched for such a system for RBBS-PC.  None seemed to be available
         out there at that time, so it looked like we'd just have to do it
         ourselves.  The original purpose was to create a small, secure,
         functional door for our users here on our own 3-node RBBS-based
         system, but our scope has since expanded quite a bit beyond what we
         had originally envisioned (to put it mildly).
         
         We acknowledge that there are at least four QWK mail doors for RBBS-PC
         message bases:
         
                JIMMER by Jim Goodenough,        (Shareware)
                TQM by Tom Collins,              (Shareware)
                our original Mail Manager, and   (Free)
                Mail Manager +Plus+              (Shareware)
         
         One of these four packages should be able to handle your QWK needs.
         Naturally, we're hoping that you choose Mail Manager +Plus+!
         
         JIMMER popped up during development of Mail Manager's initial release,
         and TQM followed a few months later.
         
         Mail Manager +Plus+ is our continuing effort to add additional
         features to the original basic Mail Manager package.  Mail Manager and
         Mail Manager +Plus+ have been in nearly continuous development since
         late January of 1991, and they are by far the largest projects that we
         have ever tackled, or are ever likely to!


     MAIL MANAGER +PLUS+ GENERAL INFORMATION                         - Page 2 -
     

         WARRANTY, DISTRIBUTION, & REGISTRATION
         --------------------------------------
         
         Mail Manager +Plus+ is NOT guaranteed in any way, shape, or form.
         Although we have worked very hard to keep our door compatible with a
         wide variety of possible RBBS configurations, we are forced to deal
         with two very important aspects of your RBBS-PC: your USERS files, and
         your MESSAGES files.  While it works just fine here, there may be
         differences in your setup that can cause problems.  THEREFORE:
         
                    RUN MAIL MANAGER +PLUS+ AT YOUR OWN RISK!
         
         The Mail Manager +Plus+ package (MPLUS310.ZIP) may be distributed
         freely (in unmodified form) to friends, associates, and bulletin
         boards.  Re-archiving into your favorite format (ARJ, LZH, etc) is
         permitted, provided that the entire package (and all documentation) is
         included in the re-archiving process, and no files are modified or
         added.  If you received this package in some other format than
         MPLUS310.ZIP, or the .ZIP file does not have -AV verification from
         Chip Morrow or Doug Wilson, then you did not receive an original copy.
         Please see Appendix B for information about Mail Manager official
         Distribution Sites where you may obtain Mail Manager +Plus+ in its
         official release form.
         
         If you are a registered user of our door, do *NOT* distribute the
         registration code that you received from us.  This is your own
         personal registration, and is not for distribution.
         
         If you are a shareware distributor/dealer, a normal disk copying and
         postage charge is permitted, provided that the amount to do so does
         not exceed the REAL costs.
         
         ----------------------------------------------------------------
         
         Mail Manager +Plus+ is a fully-functional SHAREWARE package.
         
         If you like our door, and continue using it beyond a reasonable
         evaluation period, you are obligated to register it with us.  Your
         registration will be good for future releases of the door as well.
         
         Registration of our door simply removes the "* UNREGISTERED *
         Evaluation copy" notice that you and your users see when the door
         loads, and replaces it with your registration number and name.  Mail
         Manager +Plus+ is not otherwise crippled in *ANY* way.
         
         The registration fee structure for Mail Manager +Plus+ / MNET is:
         
            Mail Manager +Plus+ alone                            = $25.00
            Mail Manager +Plus+ and MNET at same time            =  30.00
            MNET - add to existing Mail Manager +Plus+ reg.      =   7.50
                  (incl latest Mail Manager +Plus+ on disk)
            MNET by itself                                       =  10.00
         
         If you are already a registered user of Mail Manager +Plus+, and don't
         want MNET, you're all set; just download the latest version of the


     MAIL MANAGER +PLUS+ GENERAL INFORMATION                         - Page 3 -
     

         door from your favorite source.
         


     MAIL MANAGER +PLUS+ GENERAL INFORMATION                         - Page 4 -
     

         As you can see, we're not attempting to get rich here, just trying to
         cover some of the cost of development and support.  As a SysOp
         yourself, you already know what it costs for any LD connect time at
         all, and the number of hours spent in front of the keyboard.
         
         If you never intend to register Mail Manager +Plus+ with us, and/or
         need only a fraction of its features, you may wish to consider our
         "free" version of the door instead, which does not require a
         registration fee for continued use.
         
         If you do choose to register, BLESS YOU!  The registration form is on
         the next page.


     MAIL MANAGER +PLUS+ GENERAL INFORMATION                         - Page 5 -
     

         REGISTRATION FORM FOR MAIL MANAGER +PLUS+
         
                   Name:  _____________________________________________________
         
                Address:  _____________________________________________________
         
         City/State/Zip:  _____________________________________________________
         
         Mail Manager +Plus+ version that I am currently using:  _____v3.10____
         
         BBS Name (as you'd like it to appear in the registration information).
         This can be your organization name, your name, or any other one-liner
         that you would like your users to see when the door loads.  Should not
         exceed 60 characters:
         
         ______________________________________________________________________
         
         Specify disk size:  [ ] 3 1/2"    [ ] 5 1/4"
         
         Comments (optional): _________________________________________________
         
         ______________________________________________________________________
         
         ______________________________________________________________________
         
         OPTIONAL: BBS phone number and/or Zone:Net/Node ID (for our own use,
                   in case we feel it necessary to contact you directly).
         
                   ______________________________   HST [ ] v32 [ ]  2400 [ ]
         
         [ ] Mail Manager +Plus+ QWK mail door for RBBS-PC and Fido *.MSG,
             with MNET.EXE node QWK network conversion utility ......... $30.00
         
         [ ] Mail Manager +Plus+ QWK mail door for RBBS-PC and Fido *.MSG:
                                                               ......... $25.00
         
         [ ] MNET QWK network node conversion utility alone............: $10.00
         
         [ ] MNET - add to existing Mail Manager +Plus+ registration, with
             current Mail Manager +Plus+ release on disk...............:  $7.50
                 My MMGR+ registration # is _________    <-- IMPORTANT!
         
                                                       Total enclosed: ________
         
         We will mail you a copy of the current version(s) of Mail Manager
         +Plus+ (and/or MNET, if applicable), and instructions for registering
         them in the name entered above.  One registration covers all nodes of
         your BBS.
         
         Send check or money order (payable to F. D. Wilson) for total amount
         in U.S. Funds to:
                                   Makai Software
                                   870 Golden Drive
                                   Newark, OH 43055


     MAIL MANAGER +PLUS+ GENERAL INFORMATION                         - Page 6 -
     

         FEATURES/LIMITATIONS
         --------------------
         
         The length of this list got ridiculous a long time ago.  So, we'll
         only list the MAJOR stuff that you might be interested in:
         
            þ Can use a FOSSIL for communications.
            
            þ Supports both DESQview and NetBIOS file & record locking schemes,
              as well as file sharing under NetBIOS, and supports Novell
              networks.
            
            þ Mail packets can be downloaded in either text or QWK format.
              Both types of mail packets can, at the option of the sysop,
              contain all sorts of additional stuff such as bulletins, news,
              new file listings, etc.
            
            þ Supports the optional multiple message headers that are present
              in the recent release of RBBS-PC v17.4.
            
            þ Supports both types of RBBS-PC message bases, fixed-length and
              'elastic'.  (Your message bases are 'elastic' if you have
              configured them to GROW as messages are added).  Can handle a mix
              of both 'fixed-length' and 'elastic' message bases.
            
            þ Supports FIDO-style *.MSG message bases, as well as RBBS-PC's own
              *M.DEF's.
            
            þ Supports FIDO-style *.MSG netmail areas, complete with CRASH
              capability, file-attaches, and file requests.
            
            þ Each FIDO-style *.MSG area is configured with its own
              Zone:Net/Node address, so you can painlessly be a part of many
              different mail zones.  Also, AKA addresses are supported for
              Netmail areas, so crash mail can be sent to many different zones
              with a single netmail area.
            
            þ Supports QWK networks, can generate net-status-capable QWK
              packets for specific usernames.
            
            þ Special "net status" users can specify whether to receive "full"
              QWK, or just the necessities for network transfer.
            
            þ Users can read, reply, and post messages to both RBBS-PC *M.DEF
              and Fido *.MSG areas while online within the door, as well as use
              offline QWK/REP transfer of mail.
            
            þ Multi-node support (up to 36 nodes) via DORINFOx.DEF and separate
              subdirectories for each node (built by Mail Manager on-the-fly).
            
            þ Up to 500 conferences can be configured.
            
            þ Support for non-standard communication ports & IRQ's via FOSSIL,
              MAILMGR.PRO, and batch files.
            


     MAIL MANAGER +PLUS+ GENERAL INFORMATION                         - Page 7 -
     

            þ Up to 1,000 messages can be extracted & downloaded in any one
              mail packet.  Subsequent downloads will extract any additional
              waiting messages.  (1,000 messages means at least a 300K
              compressed mail packet).
            
            þ BPS rates up to 115K, and COM ports 1-4 are supported.
            
            þ X, Y, and Zmodem for file transfers via Forsberg's DSZ, or you
              can use our implementation of PROTO.DEF (MAILMGR.PRO) and
              configure a number of different protocols.
            
            þ "(R)", and "Re:", when found at the beginning of the subject
              field of extracted messages, are stripped from the field.  This
              allows offline readers to group related messages together, rather
              than into one group with and one without.
            
            þ *FAST* message extracting (in *M.DEF message bases) and handling
              of ".REP" uploads.
            
            þ High/low ASCII can be allowed or stripped in each conference.
            
            þ ANSI can be allowed or stripped in each conference.
            
            þ Mail reader tearlines in uploaded messages can be altered (for
              possible FIDO compatibility) from "--- " to "    ", or left alone
              for each conference.
            
            þ The popular "alias" merge is supported, and alias names can be
              allowed or disallowed by conference.
            
            þ Conferences can be joined from within the door, or can be
              configured to force the users to join from RBBS-PC.
         
            þ Extensive security checks.


     MAIL MANAGER +PLUS+ GENERAL INFORMATION                         - Page 8 -
     

         CHECKLIST OF REQUIREMENTS
         -------------------------
         
         [ ] DOS v3.30 or above.
         
         [ ] At least one RBBS-PC message base and user file, or if you are
             running a BBS type other than RBBS-PC, a conversion utility to
             create one for you.
         
         [ ] If you are running RBBS-PC, separate RBBS-PC users files for each
             conference/subboard.
         
         [ ] DORINFOx.DEF for remote operation.
         
         [ ] A recent version of DSZ.COM (one that supports the "handshake
             slow" command) *IN A DOS PATH!*, or the external protocols of your
             choice via MAILMGR.PRO (our implementation of RBBS-PC's
             PROTO.DEF).
         
         [ ] The environment variable of your choice set to indicate where Mail
             Manager is to look for "XFER-[node].DEF" (where [node] is the node
             number).  XFER-x.DEF is no longer required to be in the default
             directory.
         
         [ ] The file compression/extraction programs of your choice in a DOS
             path, or wherever you specified them in Mail Manager's list of
             archivers (MAILMGR.ARL).
         
         [ ] Memory:
             - About 310K free memory for Mail Manager +Plus+ itself, plus
             - 384 bytes for each conference, plus
             - whatever you need for your file compression software and
               external protocols.
             
             Think about this.  200 conferences * 384 bytes each = 76,800
             additional bytes.  That's about 386K BEFORE your external
             compression and file transfer software.  The full slew of
             conferences (500 * 384) would be an additional 192K (or a total of
             about 502K).  Figure in another RAM-hungry application like Robert
             Jung's ARJ archiver, and you could need more conventional memory
             than your PC has available!
             
             There is a wonderful shareware program available out there,
             written by Davis Augustine, by the name of "SHROOM".  SHROOM has
             the ability to swap an application to disk (or a RAM disk, for
             speed) whenever the application "shells" to an external program.
             SHROOM works very well with Mail Manager +Plus+ (RBBS-PC, too!),
             and you would be well-advised to look into this utility if you are
             tight on RAM, and/or have a large number of conferences to
             configure into Mail Manager +Plus+.
             
             You can locate SHROOM on many Bulletin Boards, or by contacting
             the author directly:
                             Davis Augustine (Shroom Shareware)
                             P.O. Box 610, Sausalito, CA 94966-0610


     INSTALLING MAIL MANAGER +PLUS+                                  - Page 9 -


         BEFORE YOU BEGIN
         ----------------
         
         **** PLEASE READ THIS!!!!!! *****************************************
         
         RBBS-PC has the unique ability to create, read, and manipulate its own
         corrupted message bases, without ever telling you that anything's
         wrong.
         
         Mail Manager is not as forgiving, and requires that your message bases
         be in good condition.  It is therefore STRONGLY suggested that you run
         some type of checkout/repair utility against your message bases BEFORE
         installing Mail Manager.  We've included an alternate utility named
         MailFix to repair/purge/renumber your message bases, which you can try
         out as an alternative to CONFIG.EXE's repair and purge functions.
         
         MailFix is compatible with RBBSMail'ed, MsgToss'ed, and OverMail'ed
         message bases (which have differently-formatted message headers), as
         well as RBBS-standard message bases, INCLUDING v17.4 multi-headers.
         This is in contrast to RBBS-PC's CONFIG option #185, which simply will
         not properly handle a message base that has been manipulated by any of
         these mail processors.
         
         *PLEASE* take a few minutes to read the section of this document
         regarding MailFix before you attempt to utilize this program!
         
         In any event, you really SHOULD check out the integrity of your
         message bases before attempting to install Mail Manager.


    INSTALLING MAIL MANAGER +PLUS+                                  - Page 10 -


         ----------------------------------------------------------------------
                          UPGRADING FROM A PREVIOUS VERSION
         ----------------------------------------------------------------------
         
         Version 3.10 is a minor update to the Mail Manager +Plus+ version 3.xx
         series.
         
         If you are upgrading from a version lower than 1.30, your best bet is
         to set up Mail Manager +Plus+ from scratch.  The changes are simply
         too extensive.  Initial installation is covered in a page or two.
         
         With that out of the way, there are several things common to ALL
         upgrades from v1.30 through 3.01:
         
             [ ] - Back up your Mail Manager directory!  It never hurts to play
                   it safe.
             
             [ ] - The main menu options have changed a bit.  If you have
                   created custom menus, change them to reflect the new option
                   lineup - de-compress the file MAILMGR.MNU from 310-
                   TXT.ZIP,and have a look at what's there.  If you are using
                   the default menus, just overwrite your existing ones with
                   MAILMGR*.MNU in 310-TXT.ZIP.
             
             [ ] - Since the main menu items have changed, the Mail Manager
                   help files have too.  Delete your old MAILMGR*.HLP files,
                   and use the new ones contained within 310-TXT.ZIP.  If you
                   are upgrading from a version earlier than 3.0, you'll notice
                   these help files have a new naming convention: MMGR*.HLP.
                   Do not rename them.
             
             [ ] - Overwrite all executables with the ones contained within
                   310-EXE.ZIP.  (You backed up your old ones, right?)
             
         MAILFIX.EXE, our message base maintenance utility has been greatly
         enhanced from the version included with earlier Mail Manager releases.
         The MNET.EXE QWK network utility has also been updated from the
         initial version included with Mail Manager v 3.0x.  You may wish to
         read the documentation on these new versions.
         
         That's it for the initial stuff.  Now, depending on which version you
         were running:


    INSTALLING MAIL MANAGER +PLUS+                                  - Page 11 -


         UPGRADING FROM THE "FREE" MAIL MANAGER v1.3x
         ---------------------------------------------
         
            Although it is relatively painless to upgrade from v1.3x of Mail
            Manager, please be aware that both the configuration file and user
            file (MAILMGR.CFG and MAILMGR.USR) have changed in format, and the
            new MAILCFG program will report that your old configuration file is
            corrupt.
            
            
            Run the supplied UPDATE.EXE against your existing configuration
            file, then run the supplied UPDATUSR.EXE against your existing
            MAILMGR.USR file.  MAKE SURE YOU RUN THESE UTILITIES FROM YOUR MAIL
            MANAGER DIRECTORY!  After you've run these utilities once, you can
            throw them away (UPDATE.EXE and UPDATUSR.EXE).
            
                      **********************************************
                --->> *  RUN UPDATUSR.EXE ONCE AND ONLY ONCE!!!!!  * <<---
                      **********************************************
            
            After that, run the new MAILCFG.EXE and carefully look for changes,
            especially in the conference edit screen.  You'll have to go into
            the new manual if some of the options appear confusing.
         
         
         UPGRADING FROM "PLUS" v2.0x:
         ----------------------------
         
            All you really need to do is run the new MAILCFG against your
            existing configuration file(s), and save your changes when
            finished.  There are two new options on the second screen of the
            main configuration:
         
               - Allow G)oodbye and E)xpedite! options to drop DTR?
                 (Default = No)
               
               - Show empty conferences? (Default = No)
         
            There are also two new options in each conference:
             
               - Number of lines allowed per message (Default = 99).  Set this
                 to zero (0) to not split long uploaded messages into smaller
                 parts.
               
               - Conference description, up to 25 characters (no default).
             
             


    INSTALLING MAIL MANAGER +PLUS+                                  - Page 12 -


         UPGRADING FROM "PLUS" v3.00 and v3.01:
         --------------------------------------
         
            There is one new option on the second screen of MAILCFG - you can
            now tell Mail Manager to display or hide empty conferences when
            your users are in the conference selection screens.
            
            Nothing else has changed since previous v3.x releases except the
            distributed PRELOG*.RBS and EPILOG*.RBS text files, which you
            probably aren't using anyway.
            
         
         IF YOU'RE SETTING UP FOR THE FIRST TIME:
         ----------------------------------------
         
         There is no such thing as a "QUICK INSTALL" for Mail Manager +Plus+,
         although you can be up and running fairly easily by:
         
             - Creating a \MAILMGR directory off of your root,
             - De-compressing the archives 310-EXE.ZIP and 310-TXT.ZIP there,
             - Run MAILCFG.EXE, and follow the prompts, then...
             - Follow standard procedure for adding a new door to your system
               (DOORS.DEF, menus, etc. etc.)
         
         However, we do *NOT* recommend that you do it this way if you have
         more than a handful of conferences, and plan to add or delete any in
         the foreseeable future.  A little advance planning *NOW* can save you
         a world of grief later, and there are many customizable text files
         that you may want to change.
         
         ----------------------------------------------------------------------
                           INSTALLING THE DOOR FROM SCRATCH
         ----------------------------------------------------------------------
         
         If for some reason these instructions are not clear to you, or this is
         your first attempt at installing a door in your RBBS-PC, there's
         really not much that can take the place of RBBS-PC's documentation.
         
         With that said...
         
         Check your environment variables (type "SET" at the DOS prompt).  Both
         RBBS-PC and Mail Manager +Plus+ use the log file "XFER-x.DEF", where
         "x" is the node number.  Mail Manager +Plus+ needs an environment
         variable to determine where this file is located on your system.  Most
         of us seem to be using Forsberg's DSZ for file transfers, so there
         should be a line referencing "DSZLOG" in either the batch file you use
         to load RBBS-PC, or your system's AUTOEXEC.BAT, which would look
         something like this for node 1:
         
            DSZLOG=C:\RBBS\XFER-1.DEF
         
               or...
         
            DSZLOG=XFER-1.DEF
         


    INSTALLING MAIL MANAGER +PLUS+                                  - Page 13 -


         If Mail Manager +Plus+ cannot find "XFER-x.DEF", it will report that
         all file transfers have failed.
         
         In any case, make a note of the environment variable name (in this
         case DSZLOG), since you'll need it later.
         
         Once you're past this, you can get on to the actual installation.
         
         Create a subdirectory just for Mail Manager +Plus+.  Stick it anywhere
         you want, and name it anything you want, just be sure that it is a
         drive and directory specifically meant for Mail Manager +Plus+.  From
         here on we'll just refer to it as the "\MAILMGR" directory.
         
         De-compress the imbedded archives "310-EXE.ZIP" and "310-TXT.ZIP" to
         the directory you just created.
         
         Now go through the motions of adding a new door to your system.  On a
         'normal' RBBS-PC this would entail:
         
            - Editing MENU5* (or whatever you have named your door menu) and
              adding the word " MAILMGR ".
            
            - Creating a MAILMGR.BAT file, and sticking it where RBBS can find
              it.  Your batch file that calls Mail Manager is very important,
              and as a minimum must logically do the following:
         
         With that in mind, a minimum batch file would look something like
         this:
         
                   cd\mailmgr
                   copy \rbbs\dorinfo%1.def
                   mailmgr %1
                   cd\rbbs
         


    INSTALLING MAIL MANAGER +PLUS+                                  - Page 14 -


         If you're running the recent "DOORS.DEF" method that RBBS-PC provides,
         here's an example line to implement Mail Manager:
         
                          MAILMGR,5,,D,"MAILMGR.BAT [NODE]",N,,
         
            This line tells RBBS-PC the following:
         
               1) The name of the door is MAILMGR.
               2) Security level 5 and above can access the door.
               3) No questionnaire is to be invoked.
               4) Exit to this door, rather than shell to it. (Mail Manager
                  requires a lot of RAM)
               5) The name of the batch file to invoke is MAILMGR.BAT.
               6) RBBS-PC is to pass the node number to the batch file.
         
                 * NOTE - Type the word "[NODE]" as shown above, and RBBS-PC
                   will replace it with the true node number when it calls the
                   batch file.  If you are running a single-node system, and
                   find this confusing, you can instead pass the node number
                   directly, but it isn't necessary to do it this way.  This
                   would make your DOORS.DEF line look something like this:
         
                          MAILMGR,5,,D,"MAILMGR.BAT 1",N,,
         
               7) Don't ask for a password when returning back to RBBS-PC.
               8) Don't display a text file when the door closes.
               9) Use the time limit from RBBS-PC as the time allowed in the
                  door.


    INSTALLING MAIL MANAGER +PLUS+                                  - Page 15 -


         IF YOU HAVE A LOCKED BPS RATE
         -----------------------------
         
         If you have your communications port locked higher than what the
         user's actual connect speed is going to be, you will find that Mail
         Manager +Plus+ will not report the correct BPS rate, nor will it
         estimate the amount of time required for file transfers properly.
         This is due to RBBS-PC passing the locked BPS rate to the door,
         instead of true connect speed.
         
         RBBS-PC versions 17.3C and lower had no provision for passing the true
         connect rate to doors.  The locked rate is always passed to
         DORINFOx.DEF.  The only way around this is to run RBBS-PC v17.4 or
         later, and modify the command line used to call Mail Manager +Plus+.
         The following will work *ONLY* with RBBS-PC v17.4 and up! (or with
         copies of RBBS-PC compiled with the CBAUD merge):
         
         Change the DOORS.DEF example mentioned on page 10 to read:
         
                 MAILMGR,5,,D,"MAILMGR.BAT [NODE] [CBAUD]",N,,
         
         Then, in your batch file that loads the door:
         
                 mailmgr %1 /CBAUD%2
         
         If the door is called on node 2 of your system, and the user's connect
         rate is 2400 BPS, the above line will look like this to Mail Manager
         +Plus+:
         
                 mailmgr 2 /CBAUD2400
         
         With this done, your basic door installation is finished, and the time
         has come to plan your interface for the users, and to configure the
         door for your system.


    INSTALLING MAIL MANAGER +PLUS+                                  - Page 16 -


         COMMAND LINE OPTIONS
         --------------------
         
         Mail Manager +Plus+ has several different available command line
         options.  You will never use all of them at once, but variations of
         these can be useful for the various operations that the door is
         capable of performing.
         
           MAILMGR [Node] [/I] [/O] [/A] [/CBAUDxxxxx] [/WX:\PATH]
         
              Node = The node number currently in use. (1, 2, 3, etc.)
              
                /I = "Import mode".  Most useful when operating in local mode,
                      this option causes the door to immediately process a REP
                      packet that is waiting in the proper work directory.
              
                /O = "Output mode".  Most useful when operating in local mode,
                      this option causes the door to immediately extract mail
                      from your selected conferences, creating a new mail
                      packet.
              
                /A = "Automatic mode".  Again, most useful in local mode.  This
                      option causes the door to go straight into E)xpedite
                      mode, which will process any waiting .REP, and also
                      extract any new waiting mail.
              
              /CBAUD = An option that became available with the advent of RBBS-
                      PC's template variable "[CBAUD]", which is the true
                      connect rate of the user.  This option can be used in
                      your DOORS.DEF as follows, but ONLY IF YOU ARE RUNNING A
                      VERSION OF RBBS-PC THAT SUPPORTS THE [CBAUD] VARIABLE!:
                      
                                           /CBAUD[CBAUD]
                      
                      Then, if the user were connected at 2400 bps on your
                      system, Mail Manager +Plus+ would see it like so:
                      
                                            /CBAUD2400
                      
                      This makes the door capable of accurately determining
                      transfer times for your users.
              
                 /W = Drive/path to use for work directories.  Mail Manager
                      +Plus+ normally creates and manipulates files in separate
                      directories off of the directory in which you installed
                      door.  If you are tight on disk space on this drive, or
                      would rather use a ram disk for a work drive, you can
                      specify this option.  NOTE - If you implement this
                      option, and intend to use a RAM disk for a work drive, it
                      had best be a BIG one indeed!  Don't forget that a single
                      MESSAGES.DAT can be over 1 meg in size, plus the archived
                      mail packet itself.  If you run out of room, you will not
                      be able to pack/unpack the QWK or REP packet.
                      
                      To use drive "X" as your work drive, this command would


    INSTALLING MAIL MANAGER +PLUS+                                  - Page 17 -


                      look like this:
                                           /WX:
                      
                      The door *will* create separate work subdirectories (such
                      as \LOCAL, \NODE1, etc.) off of what you specify here.
                      In the above example, X:\LOCAL, X:\NODE1, etc. would be
                      used as your work directories.  You can specify a
                      specific path to use as the base for these directories,
                      if you do not want them off the root of your work drive.
                      
                      If you do not use this option, Mail Manager +Plus+ will
                      create the work directories off of the directory that you
                      installed the door in
         
         Sample command lines, based on the above:
         
           MAILMGR  - No command line always assumes local operation.  Door
                      will come up in local mode, using the sysop name as
                      listed in the configuration file.  Any mail packets
                      created during the session will be placed in the \LOCAL
                      work directory, as mentioned above.
           
           MAILMGR /A  - Local mode, automatic operation.  Goes straight into
                      expedite mode, then returns to DOS.  Processes any
                      waiting .REP in the \LOCAL work directory, and will also
                      create a mail packet there if there was any new unread
                      mail waiting to be picked up.
           
           MAILMGR 1 /o  - Read DORINFO1.DEF for operating parameters, create a
                      new mail packet in the \NODE1 work directory, and return
                      to DOS.
           
           MAILMGR 1 /i  - Read DORINFO1.DEF for operating parameters, process
                      any waiting .REP packet in the \NODE1 work directory, and
                      return to DOS.
           
           MAILMGR 5 /CBAUD14400 /wD:\WORK  - Read DORINFO5.DEF for operating
                      parameters, tell the door that the connect rate is 14400
                      bps, and use D:\WORK as the base drive/dir for the door's
                      work directories.  The program will use D:\WORK\NODE5 as
                      its work directory.
           
         By careful, planned use of these options, and "dummy" DORINFOx.DEF
         files with the communications port configured as COM0, you can do some
         mighty advanced stuff via batch files.  Some thoughts that come
         immediately to mind are "prescanned" mail packets for specific users,
         and automatic operation of QWK networking.  As you become more
         familiar with the door, and begin using it yourself in local mode as
         the sysop, more and more of these options are likely to become useful
         to you.


    INSTALLING MAIL MANAGER +PLUS+                                  - Page 18 -


         PLANNING YOUR USER INTERFACE
         ----------------------------
         
         As with most aspects of your RBBS-PC, you will get the best results
         from Mail Manager +Plus+ with a little advance planning.  To your
         users, the single most important aspect of Mail Manager will be the
         ability to locate which conferences they want to follow.  This sounds
         simple enough, but think about that for a second, especially if you're
         running a system with more than a handful of conferences.
         
         Here are some serious points to consider BEFORE diving into the
         configuration program:
         
             1 - Your RBBS-PC MAIN message base must ALWAYS be configured as
                 conference #1.  This is VERY IMPORTANT - Mail Manager +Plus+
                 simply will not function properly if your MAIN area is not #1
                 on the list.  The door uses the information found in the MAIN
                 area for some of its default functions for each user.  If you
                 are not running RBBS-PC, your conversion utility that loads
                 the door must be capable of creating RBBS-PC users and
                 messages files, which you would configure as area #1.  The
                 user file created in this operation MUST (as a minimum)
                 contain information for the user that is loading the door.
             
             2 - Once MailCFG creates your configuration file, and your users
                 start using the door, you cannot easily re-sort your
                 conferences.
             
             3 - If you have several different TYPES of conferences (such as
                 local, RBBS-NET, FIDO-NET, etc.), you'll want to consider how
                 to group the conferences together for the user's purposes.
             
             4 - Will you be adding more conferences at some point?  Will you
                 want those conference names to be inserted in the middle of
                 your list of conference numbers?  It is easy to tack
                 conferences onto the end, but to insert them in the middle
                 requires a little forethought to leave skip empty conference
                 numbers *NOW*.
             
             5 - After Mail Manager +Plus+ has been running for a while, and
                 you decide to delete a conference, delete it, but RESERVE THE
                 SPACE FOR THAT CONFERENCE NUMBER!!!  If you don't, your
                 conferences will be re-numbered, and the unsuspecting users
                 might inadvertently upload a reply to the wrong conference
                 number.
         
         If all this is too much to think about for the moment, consider this
         relatively simple example...  Say you have a total of 3 conferences:
         
               1 MAIN message base, 1 RBBS-NET area, and 1 FIDO-NET area.
         
         Now, if you think at some point that you might add two more
         conferences to your list of RBBS-NET conferences, and maybe five more
         local areas, here's how you might want the conference numbers to look
         from Mail Manager's standpoint:


    INSTALLING MAIL MANAGER +PLUS+                                  - Page 19 -


              1 - MAIN     - My main message base
              2 -  ---
              3 -  ---
              4 -  ---
              5 -  ---
              6 -  ---
              7 - RBBSNET  - An RBBSNet conference
              8 -  ---
              9 -  ---
             10 - FIDONET  - A FidoNet conference
         
         Now, when you do add an extra local conference, you can insert it in
         position #2, 3, 4, 5, or 6.
         
         Otherwise, your conferences will be ordered as:
         
              1 - MAIN
              2 - RBBSNET
              3 - FIDONET
         
         ... and you would have to tack that new local conference on at
         position #4.  Starting to make sense now?
         
         OK... with that in mind, if you have a CONFMAIL.DEF file (RBBS-PC's
         list of conferences), copy it to your Mail Manager directory, and take
         a look at it.  If you don't have a CONFMAIL.DEF, go ahead and skip
         this section.
         
         Are your conference types grouped together?  Do you want to leave
         spaces between any of them?
         
         Now's the time to sort it however you see fit, making sure that your
         MAIN area is the very first one listed, at the top of the file.
         
         If you want to add empty conference numbers between any of them, add
         the following line:
         
                     {EMPTY}U.DEF,
         
         MailCFG will reserve that spot for future use.  Using a real quick
         example, say you have two conferences, and your current CONFMAIL.DEF
         looks like this:
         
                      C:\RBBS\MAINU.DEF,C:\RBBS\MAINM.DEF
                      C:\RBBS\BBSADSU.DEF,C:\RBBS\BBSADSM.DEF
         


    INSTALLING MAIL MANAGER +PLUS+                                  - Page 20 -


         If you wanted to reserve a space between these two, you would edit
         CONFMAIL.DEF (the one that you copied to Mail Manager's directory,
         obviously) to look like this:
                      C:\RBBS\MAINU.DEF,C:\RBBS\MAINM.DEF
                      {EMPTY}U.DEF,
                      C:\RBBS\BBSADSU.DEF,C:\RBBS\BBSADSM.DEF
         
         Mail Manager will see conference #2 as empty, and you'll be able to go
         back into MailCFG to add it in later.  DON'T FORGET THE COMMA AFTER
         {EMPTY}U.DEF !!
         
         Last thing to note here is that Mail Manager displays conferences to
         the users in either columns of 10, like so:
         
               1               11              21
               2               12              22
               3               13              etc..
               4               14
               5               15
               6               16
               7               17
               8               18
               9               19
              10               20
         
         ...or in groups of 15 if they are viewing conference descriptions:
         
               1 MAIN    - My main message base
               2 CONF2   - My second conference
               3         - (etc. etc. etc.)
               4         -
               5         -
               6         -
               7         -
               8         -
               9         -
              10         -
              11         -
              12         -
              13         -
              14         -
              15         -
         
         If you have a large number of conferences, you may want to take this
         into consideration as well.
         
         Once you have prepared CONFMAIL.DEF for Mail Manager +Plus+ as
         mentioned above, you can import it into the configuration program
         (MAILCFG.EXE).  BEFORE YOU DO THIS, set up your text files that Mail
         Manager +Plus+ is to use (see next page).
         
         One last thing to mention here is that CONFMAIL.DEF is not used by
         Mail Manager +Plus+ itself at all.  Once you have imported your
         conferences into the MAILCFG.EXE program, Mail Manager +Plus+ will
         never look at your CONFMAIL.DEF again.


    INSTALLING MAIL MANAGER +PLUS+                                  - Page 21 -


         SYSOP-CONFIGURABLE TEXT FILES
         -----------------------------
         
         The last step before getting into the configuration program is to set
         up your text files, and Mail Manager +Plus+ uses quite a few.  Here
         goes:
         
             (All in Mail Manager's directory)
         
             MMGR1.HLP  \ _   The online help files that will be displayed to
             MMGR2.HLP  /     users when "H" and "?" are selected from the main
                              menu.  You can customize if need be, but they
                              should be pretty much OK as-is.
         
             MAILMGR.PRE    - The initial screen displayed when Mail Manager
                              loads.  Again, you might want to customize it for
                              your own individual system, but it is generic
                              enough as distributed that you may not need to.
                              If this file (and the corresponding graphic and
                              ANSI versions) do not exist, Mail Manager +Plus+
                              will take the user Directly to the main menu
                              after it loads.  Otherwise, this screen will be
                              displayed, and the prompt "Press any key to
                              continue..." will be shown.
             
             MAILMGR.MNU    - Mail Manager's main menu, displayed to the users
                              just before the command prompt.
             
             PRELOG.RBS     - The welcome message that your users will see when
                              they first fire up their mail reader against one
                              of Mail Manager's QWK's.  Probably the most
                              common thing that you'd want to put here would be
                              a copy of your RBBS-PC prelog or welcome screen,
                              but this is entirely up to you!
             
             EPILOG.RBS     - The signoff message that the users will see just
                              as they exit your QWK packet from their mail
                              reader.  You might want to put an adaptation of
                              RBBS-PC's EPILOG.DEF here.
         
             MMGR1G.HLP    \
             MMGR2G.HLP     \
             MAILMGRG.PRE    \ ASCII graphic versions of the above.
             MAILMGRG.MNU    / (Optional)
             PRELOGG.RBS    /
             EPILOGG.RBS   /
         
             MMGR1C.HLP    \
             MMGR2C.HLP     \
             MAILMGRC.PRE    \ Color/ANSI versions of the above.
             MAILMGRC.MNU    / (Optional)
             PRELOGC.RBS    /
             EPILOGC.RBS   /


    INSTALLING MAIL MANAGER +PLUS+                                  - Page 22 -


             MAILMGR.BUL    - The list of bulletin path/filenames that you'll
                              want to include in your users' QWKs.  Edit this
                              file to pertain to your system bulletins (and/or
                              any other text files that you'll want to include
                              in your users' QWK packets), and if any of them
                              are newer than the user's last call to RBBS-PC,
                              the user will get them included in his/her QWK
                              packet.
                              
                              Bulletins preceded with a double-asterisk are
                              considered mandatory for inclusion in the user's
                              mail packets, and if new, they will be included
                              regardless of whether the user has configured
                              Mail Manager to send new bulletins.
                              
                              Example:
                              
                                  c:\bulet1
                                  c:\bulet2
                                  **c:\bulet3
                              
                              bulet1 and bulet2 are optional, bulet3 will
                              always be included if it has been updated.
                              
                              (NOTE - The path\filename of MAILMGR.BUL is
                              sysop-configurable in MailCFG.EXE.)
             
             MAILMGR.PRO    - A copy of the RBBS-PC PROTO.DEF that you intend
                              to have Mail Manager +Plus+ use.  Mail Manager
                              +Plus+ can use all of RBBS-PC's "template"
                              variables in here, such as [NODE], [PORT#],
                              [BAUD], [CBAUD], etc.  Refer to the RBBS-PC
                              documentation for information on these "template"
                              variables.
                              
                              For the purposes of Mail Manager +Plus+, it is
                              important that you configure "N)one" as the last
                              protocol in this file!  You will also need to
                              configure an external X)modem and Y)modem, since
                              Mail Manager obviously cannot use RBBS-PC's
                              internal X and Y that are probably listed in your
                              existing RBBS-PC PROTO.DEF.  See the sample
                              MAILMGR.PRO for an example of how to configure
                              these protocols externally using DSZ.
                              
                              If you are running multiple nodes, with different
                              communication port setups, you may want to create
                              copies of this file with the necessary arguments
                              changed accordingly (MAILMGR1.PRO, MAILMGR2.PRO,
                              etc.).
                              
                              (NOTE - The path/filename of MAILMGR.PRO is
                              sysop-configurable in MAILCFG.EXE).


    INSTALLING MAIL MANAGER +PLUS+                                  - Page 23 -


             MAILMGR.ARL    - The list of archivers that are available to your
                              users through Mail Manager +Plus+.  MAILMGR.ARL
                              is a "template" file, similar in structure to
                              MAILMGR.PRO.
                              
                              The supplied copy of MAILMGR.ARL allows the use
                              of ARC, ARJ, LZH, and ZIP compression methods,
                              which the user can pick and choose from to suit
                              their own preference.  You can configure fewer or
                              additional archivers as you see fit.  Format of
                              each line:
                              
                                         Name, EXT, Compress, Extract
                              
                              Name = The name of the archiver, as shown to the
                                user.
                              EXT = The three-letter extension that this
                                archiver creates by default for compressed
                                files.
                              Compress = The line to send to DOS to compress
                                the mail packets.
                              Extract = The line to send to DOS to extract the
                                uploaded reply packets that the user uploads.
             
                              "Template" variables that can be included in the
                                Compress and Extract lines (Mail Manager will
                                convert these to their true values):
             
                                [FILE]  - Compressed file to create, or extract
                                  from.
                                [INC]   - All files that Mail Manager normally
                                  includes in the downloadable archive.
                                [REPLY] - Reply file that Mail Manager expects
                                  to be contained within the compressed upload.
                                [NODE]  - Current RBBS-PC node number.
             
                              See the supplied MAILMGR.ARL for an example
                              implementation of this file.
                              
                              (NOTE - The path/filename of MAILMGR.ARL is
                              sysop-configurable in MAILCFG.EXE).


    INSTALLING MAIL MANAGER +PLUS+                                  - Page 24 -


         TEXT FILES RELATED TO FIDO *.MSG NETMAIL AREAS
         ----------------------------------------------
         
         Mail Manager +Plus+ has two system text files that pertain only to
         FIDO-style netmail areas.  If you are not running any of these types
         of areas, these two files need not exist.  Otherwise, Mail Manager
         +Plus+ will look for both of these in your Mail Manager directory.
         
             MMGRNODE.AKA     List of "AKA" addresses that your system uses.
                              If you are a member of more than one network, you
                              may wish to make use of this file for your
                              netmail areas.  This is a simple text file,
                              listing all of the Zone:Net/Node numbers that
                              pertain to your system.  It's format is as
                              follows (flush left in the file):
                              
                                   1:226/1400
                                   8:965/9
                                   10:10/1
                              
                              This would inform Mail Manager that you are a
                              member of three different networks, zones 1, 8,
                              and 10.  Any netmail message addressed to zone 8
                              would cause Mail Manager +Plus+ to temporarily
                              change your ID to "8:965/9" for that particular
                              message, regardless of the zone:net/node ID that
                              you configured that netmail area in the MAILCFG
                              program.
                              
                              Only one address per mail zone can be listed
                              here, since Mail Manager +Plus+ will use the
                              first one it finds.  For instance, if you set
                              this file to read:
                              
                                   1:226/1400
                                   1:226/1401
                                   8:965/9
                                   10:10/1
                              
                              ... Mail Manager +Plus+ will always use the "AKA"
                              of 1:226/1400 for netmail messages addressed in
                              zone 1, since that is the first zone 1 address
                              listed.  See the example MMGRNODE.AKA included in
                              this package for a sample implementation of this
                              file.  If MMGRNODE.AKA is not found in your Mail
                              Manager directory, the Zone:Net/Node address
                              listed in the configuration file for that
                              conference will be used at all times.
             


    INSTALLING MAIL MANAGER +PLUS+                                  - Page 25 -


             MMGRNODE.OB      The list of outbound directories that your system
                              uses.  This file informs Mail Manager +Plus+
                              where to place CRASH messages, and file
                              attach/request packets.  If this file is not
                              found (or not configured properly), you will be
                              unable to send CRASH netmail.
                              
                              The format of MMGRNODE.OB is as follows (again,
                              flush left):
                              
                                   Zone, X:\PATH\OUTBOUND.DIR
                              
                              So, if you are in three separate mail zones, your
                              MMGRNODE.OB file might look like this:
                              
                                   1, C:\BINKLEY\OUTBOUND
                                   8, C:\BINKLEY\OUTBOUND.008
                                   10, C:\BINKLEY\OUTBOUND.010
                              
                              A trailing backslash on the directory name is
                              optional.


    CONFIGURING MAIL MANAGER +PLUS+ (MAILCFG.EXE)                   - Page 26 -


         Mail Manager +Plus+'s configuration file (MAILMGR.CFG) is binary in
         nature (for FAST loading), and can be directly manipulated by the
         supplied program, MAILCFG.EXE.
         
         Since many SysOps are VERY accustomed to using text editors against
         the various configuration files on their systems, we have managed to
         catch quite a bit of unexpected flak about the way MAILCFG does
         things.
         
         We decided in the end that the best thing to do would be to give you
         two options:
         
             MAILCFG.EXE - Manipulate the configuration file directly, or use
                           the following pair of executables:
             
             CFG2TXT.EXE - Convert MAILMGR.CFG to a text file.
             TXT2CFG.EXE - Convert a text configuration file to MAILMGR.CFG.
         
         MAILCFG.EXE is the recommended way to go, so the following
         instructions pertain to the use of this program.  The other pair of
         programs are covered in the section of this document entitled:
         "UTILITY PROGRAMS BUNDLED WITH MAIL MANAGER +PLUS+".
         
         Change to your Mail Manager directory, and run MAILCFG.EXE.
         
         The first time you fire up MAILCFG, it isn't going to find the
         configuration file, MAILMGR.CFG.  MAILCFG will report to you as such,
         and ask you if this is a first-time setup.  (Just answer "Y" at this
         point).
         
         Just for the record, if you tell it "N", (this is not a first-time
         setup), MAILCFG will figure that you started it from the wrong
         directory, and will ask you for the correct path/name to MAILMGR.CFG.
         
         After you press "Y", MAILCFG will prompt you whether to A)uto-config,
         or M)anually configure your conferences.
            
            A)uto   - If you're not familiar with RBBS' CONFMAIL.DEF, ignore
                      this option, and choose M)anual instead.
                      
                      This option will let you choose the path\filename of your
                      CONFMAIL.DEF, and then ask you for default values to
                      auto-create for EVERY conference.  This can save LOTS of
                      time if you have many conferences to configure into Mail
                      Manager.
                      
                      SUGGESTION:  At this point, you should key in the
                      path/name to THE EDITED COPY of CONFMAIL.DEF that you
                      created a few pages back.
                      
                      MailCFG will then step through your CONFMAIL.DEF and set
                      things up for Mail Manager +Plus+'s use.  The ONE
                      REQUIREMENT for using CONFMAIL.DEF is that your MAIN
                      message base absolutely *MUST* be the first conference
                      listed!


    CONFIGURING MAIL MANAGER +PLUS+ (MAILCFG.EXE)                   - Page 27 -


            
            M)anual - Will create a default configuration file, and require you
                      to manually add all of your conference information.
                      
                      If you have FIDO *.MSG conferences to add to your Mail
                      Manager +Plus+ configuration, and would like to auto-
                      import them in the same manner as above, you should first
                      set up all of your RBBS-PC *M.DEF areas via CONFMAIL.DEF
                      as above, read through this section so that you will know
                      what each option is for, and then read up on the section
                      of this document specific to FIDO *.MSG message areas.
         
         Now let's talk about MAILCFG.EXE itself.
         
         There are four main screens.  Use the cursor keys to move around in
         each one.  [Esc] always takes you back to the previous level. [PgUp]
         and [PgDn] usually lets you switch screens.  Starting on the next
         page, we'll take each one individually.


    CONFIGURING MAIL MANAGER +PLUS+ (MAILCFG.EXE)                   - Page 28 -


         ---------------------------------------------------------------------
              MAILCFG SCREEN 1 - GENERAL CONFIGURATION (Screen #1 of 2):
         ----------------------------------------------------------------------
         
         Unless you're configuring Mail Manager +Plus+ for the first time, this
         is the screen that pops up when you load MAILCFG.  It looks something
         like this:
         
           Name of your BBS................ : RBBS-PC
           Remote Sysop Name............... : SECRET LOGONNAME
           Sysop First Name................ : SYSTEM
           Sysop Last Name................. : OPERATOR
           Security to read ALL messages... : 10
           Security to use in local mode... : 10
           Use ANSI graphics in local mode? : Y
           Tagline : Your friendly neighborhood RBBS-PC - (123) 555-1212
           Network type (local mode only).. : DOS
           Filename to use for extracts.... : RBBS-PC
           Default file compression........ : ZIP
           Path/Name of your NEWS file .... : C:\RBBS\MAIN.NWS
           Path/Name of your FMS directory. : C:\RBBS\MASTER.DIR
           Handshake method (F, R, X, N)... : XON/XOFF
         
             Next Screen       Edit Conference selections          Exit
         
         ----------------------------------------------------------------------
         
         Now to take these one at a time:
         
           - Name of your BBS................ :
         
                 This should be the name of your board as set in RBBS CONFIG.
                 You can stick anything in here, however.  This name will be
                 shown to the user several times, and will be shown in the
                 offline mail reader as the board name.
         
           - Remote Sysop Name............... :
         
                 This *MUST* be the full name that you use to log on remotely.
                 Mail Manager +Plus+ will not operate properly if it cannot
                 find you (the SysOp) in the various users files.
         
           - Sysop First Name................ :
         
                 Your first name as you are known to your users.
         
           - Sysop Last Name................. :
         
                 Your last name as you are known to your users.
         


    CONFIGURING MAIL MANAGER +PLUS+ (MAILCFG.EXE)                   - Page 29 -


           - Security to read ALL messages... :
         
                 * A VERY IMPORTANT SECURITY LEVEL! *
                 
                 This should be set to either SYSOP or CO-SYSOP level only!
                 Anyone with this security level or higher can read any message
                 addressed to any user, regardless of whether or not it's
                 private!
                 
                 Mail Manager +Plus+ also uses this security level for most of
                 it's SysOp-only functions, such as the ability to use the
                 I)nfo option from Mail Manager +Plus+'s main menu.
         
           - Security to use in local mode... :
                 
                 Should be set to SYSOP level.  Whenever Mail Manager +Plus+ is
                 brought up locally, it will use this security level, and the
                 SysOp name(s) as listed above.
                 
           - Use ANSI graphics in local mode? :
         
                 Either "Y" or "N", and pretty self-explanatory, I think.
         
           - Tagline :
                 
                 This can be anything that you'd like to stick on the bottom of
                 all messages.  (Usually a very brief BBS advertisement).  If
                 this is left blank (or "NONE"), Mail Manager will not append a
                 tagline to the bottom of each message that the user downloads.
                 
                 Please note that taglines can be different in each conference.
                 This is simply what you use as a default.
         
           - Network type (local mode only).. :
         
                 This setting affects local operation only.  Valid settings
                 are:
         
                   D = DOS - No file/record locking in place.
                   Q = DESQview - Use DESQview resource locking.
                   N = NetBIOS - Use NetBIOS file/record locking, and
                        implement file sharing.  Unless you're running
                        in a Novell network, this option requires that
                        DOS SHARE be installed.
         
                 Type of network is fully explained elsewhere in this document.
         


    CONFIGURING MAIL MANAGER +PLUS+ (MAILCFG.EXE)                   - Page 30 -


           - Filename to use for extracts.... :
         
                 Specify up to 8 characters here.  All downloaded files will
                 begin with this filename.  You might want to abbreviate your
                 board name here to make it clearer to the users once they've
                 downloaded their file(s).
                 
                 Using "MYBBS" for an example, QWK downloads would be named
                 MYBBS.QWK, and text extracts would be named MYBBS.ZIP, ARJ,
                 etc.
                 
                 Also, all uploaded replies will be expected to have this
                 filename, with the extension ".REP".  Any uploads that don't
                 have an exact match on filename are ignored.
                 
           - Default file compression........ :
         
                 Must be three characters, and one of the following:
                 
                    ARC - Use Katz's PKARC.
                    ARJ - Use Jung's ARJ.
                    LZH - Use Yoshi's LHARC.
                    ZIP - Use Katz's PKZIP/PKUNZIP.
                 
                 Unless you use Mail Manager +Plus+'s list of archivers, all
                 downloads will be compressed using this format, and all
                 uploads will be expected to be in this format.  The archiver
                 of your choice absolutely *MUST* be in a DOS path if you are
                 not using the list of archivers!  Just sticking it in the Mail
                 Manager directory won't do.  If you are using the list of
                 archivers, Mail Manager will use the archiver list to
                 determine how to call the archiver.
                 
           - Path/Name of your NEWS file.... :
                 
                 Type in the full path to the *NON-GRAPHIC VERSION* of your
                 RBBS-PC news file (usually MAIN.NWS in your RBBS-PC bulletin
                 directory).  If the user is using ASCII or ANSI graphics, Mail
                 Manager +Plus+ will automatically attempt to pick up the
                 appropriate graphic version of this file for them.  If this
                 file is newer than the user's last logon, it will be included
                 in their QWK packets.  Otherwise it will be skipped when their
                 QWK packet is created.
         
           - Path/Name of your FMS directory :
         
                 If you are using an RBBS-standard FMS directory, and would
                 like to make a list of new files available to your users
                 (since their last trip into the Mail Manager door), key in the
                 full path/filename of your FMS directory here.  If you do not
                 want to use this option, leave this blank, or key in the word
                 "NONE" (with no quotes).
         


    CONFIGURING MAIL MANAGER +PLUS+ (MAILCFG.EXE)                   - Page 31 -


           - Handshake method (F, R, X, N)... :
                 
                 Allows you to specify the type of flow control that you'd like
                 Mail Manager +Plus+ to use.  The four possible settings are as
                 follows:
                 F = FOSSIL  Mail Manager will always try to use a FOSSIL with
                        this setting.  If Mail Manager +Plus+ is unable (for
                        whatever reason) to initialize your FOSSIL driver, it
                        will default to XON/XOFF.
                        
                 R = RTS/CTS    (Use request to send/clear to send)
                 X = XON/XOFF   (Use XON/XOFF)
                 N = NONE       (No handshaking)
                 
                 If set to R, X, or N:
                    
                    The FOSSIL argument is passed to Mail Manager from RBBS-PC
                    in the DORINFOx.DEF file.  If Mail Manager finds that a
                    FOSSIL is active in RBBS-PC, it will automatically attempt
                    to utilize the FOSSIL, regardless of this setting.
                    
                    Mail Manager will default back to this setting if it is
                    unable to use your FOSSIL driver.
                 
                 Use of a FOSSIL with Mail Manager is further explained
                 elsewhere in this document.
         
           - Next Screen
         
                 Position the cursor over this option, press [ENTER], and you
                 will be taken to the second general configuration screen.
         
           - Edit Conference selections
         
                 Position the cursor over this option, press [ENTER], and you
                 will be taken to the conference selection screen.
         
           - Exit
         
                 Position the cursor over this option and press [ENTER] (or
                 press [Esc] from anywhere on this screen), and you'll be asked
                 to save your configuration before MAILCFG exits to DOS.
         
         Thus endeth screen #1.


    CONFIGURING MAIL MANAGER +PLUS+ (MAILCFG.EXE)                   - Page 32 -


         ----------------------------------------------------------------------
              MAILCFG SCREEN 2 - GENERAL CONFIGURATION (Screen #2 of 2):
         ----------------------------------------------------------------------
         
         This screen should look something like this:
         
           Path/Name of your bulletin list. : C:\MAILMGR\MAILMGR.BUL
           Path/Name of protocol definitions: C:\MAILMGR\MAILMGR.PRO
           Path/Name of list of archivers...: C:\MAILMGR\MAILMGR.ARL
           Environment variable to check....: DSZLOG
           Modify uploaded msgs date/time? .: No
           Location of your BBS.............: Anytown, USA
           BBS Phone number (xxx-xxx-xxxx)..: 123-456-7890
           Smart text character (1-255).....: 123
           Default path to RBBS-PC msg bases: C:\RBBS\
           Log file for FIDO conferences....: NONE
           Door is timelocked from (xx:xx)..: 00:00
                                to (xx:xx)..: 00:00
           Allow G)oodbye to drop DTR? .....: No
           Show empty conferences? .........: Yes
         
             Previous Screen       Edit Conference selections          Exit
         
         ----------------------------------------------------------------------
         
         Now to take these one at a time:
         
           - Path/Name of your bulletin list :
         
                 Type in the full path to your list of bulletins that you would
                 like to include to your users in their QWK packets.  This is a
                 text file, and simply lists the paths and names of the *NON-
                 GRAPHIC VERSIONS* of your commonly updated bulletins. (The
                 door will automatically pick up the ASCII or ANSI versions of
                 your bulletins, depending on the user's graphic preference).
                 The default is MAILMGR.BUL in a directory named C:\MAILMGR.
                 This file should look something like this:
                 
                   C:\RBBS\BULLET1
                   C:\RBBS\BULLET2
                   C:\RBBS\BULLET3
                   **C:\RBBS\ALWAYS.BUL
                 ... etc.
                 
                 The date stamp on these files will be checked against the last
                 logon date of the user, and if they are determined to be the
                 same as (or newer than) the user's last logon date, they will
                 be included in his/her QWK packet.
                 
                 Bulletins preceded with a double-asterisk "**" are deemed as
                 "mandatory for inclusion", and will be included in the user's
                 mail packets (if they are newer than the user's last date into
                 the door) regardless of whether or not the user has turned
                 "off" the ability to receive new bulletins.
                 


    CONFIGURING MAIL MANAGER +PLUS+ (MAILCFG.EXE)                   - Page 33 -


                 Bulletins without the leading double-asterisk are deemed as
                 "optional", and will not be sent to the user if they have
                 turned "off" the ability to receive new bulletins.
         
           - Path/Name of protocol definitions :
         
                 Type in the full path to the RBBS-PC PROTO.DEF that you wish
                 to use with Mail Manager +Plus+.  The supplied file
                 MAILMGR.PRO allows X, Y, and Zmodem via DSZ.  The very last
                 protocol letter listed in this file MUST be "N", for none.
         
           - Path/Name of list of archivers...:
         
                 Type in the full path to Mail Manager +Plus+'s list of
                 archivers (default is MAILMGR.ARL in the C:\MAILMGR
                 directory).  If you do not want to give your users the option
                 of which compression format to use, leave this line blank, or
                 enter "NONE" (no quotes), and Mail Manager will use only your
                 default type of file compression.
                 
                 See the section of this document entitled "SYSOP-CONFIGURABLE
                 TEXT FILES" for further details regarding the format of
                 MAILMGR.ARL.
                 
           - Environment variable to check....:
         
                 Key in the name of the environment variable that Mail Manager
                 +Plus+ is to check to determine where to look for "XFER-
                 x.DEF".  Most of us seem to be using Forsberg's DSZ for
                 transfers, so in this case you would key in the default name
                 of "DSZLOG".
                 
                 When you're finished configuring Mail Manager +Plus+, check
                 your environment variable to insure that it points to XFER-
                 x.DEF.  Without XFER-x.DEF, Mail Manager +Plus+ will assume
                 that all file transfers have failed.
         
           - Modify uploaded msgs date/time?
         
                 Either "Y" or "N".  Setting to "Y" tells Mail Manager +Plus+
                 to use your computer's current system date and time for all
                 uploaded replies.  Setting to "N" tells Mail Manager +Plus+ to
                 use the date and time stamp as it was received in the uploaded
                 reply packet.
         
                 Advantage:  Having Mail Manager +Plus+ modify this field
                     assures that all uploaded messages will have the correct
                     date and time stamp applied before inserting into your
                     message base(s).
                 
                 Disadvantage:  If a user uploads several replies in the same
                     mail packet (many do), some mail networks (like FIDO-NET)
                     will have trouble with several messages containing the
                     exact same date & time stamp, and will likely refuse
                     everything but the first msg of the "offending" group.  If


    CONFIGURING MAIL MANAGER +PLUS+ (MAILCFG.EXE)                   - Page 34 -


                     you're a member of one of these networks, you'll probably
                     want to take the date/time stamp as-received from the
                     user.
         
           - Location of your BBS
         
                 The City, State in which your system is located.  This is
                 added to the CONTROL.DAT file that is included in all QWK
                 packets, is part of the QWK standard, and is not used anywhere
                 else by Mail Manager +Plus+.
         
           - BBS Phone number (xxx-xxx-xxxx)
         
                 The phone number to your system.  This is also added to the
                 CONTROL.DAT file that is included in all QWK packets, is part
                 of the QWK standard, and is not used anywhere else by Mail
                 Manager +Plus+.
         
           - Smart text character (1-255)
         
                 The ASCII value of the "lead-in" character for RBBS-PC smart
                 text.  RBBS-PC default for this value is "123", which is the
                 "{" character.  This value must match what you are using with
                 RBBS-PC, or smart text in bulletins and news files will not be
                 converted properly.
                 
                 Mail Manager +Plus+ will attempt to replace all possible
                 "smart text" variables with their true values in bulletins and
                 news files.
                 
           - Default path to RBBS-PC msg bases
                 
                 This should be set to the path where your *M.DEF message bases
                 are located.  MAILCFG.EXE will then attempt to save you some
                 keyboard entry time by "guessing" the true path/filename of
                 all conferences entered manually.
                 
                 For instance, if this value is set to "C:\RBBS\", and you
                 configure a conference named BBSADS, MAILCFG.EXE will "guess"
                 the path/name of the users file as:
                 This should be set to the path where your *M.DEF message bases
                 are located.  MAILCFG.EXE will then attempt to save you some
                 keyboard entry time by "guessing" the true path/filename of
                 all conferences entered manually.
                 
                 For instance, if this value is set to "C:\RBBS\", and you
                 configure a conference named BBSADS, MAILCFG.EXE will "guess"
                 the path/name of the users file as:
                 
                 
                     C:\RBBS\BBSADSU.DEF
                 


    CONFIGURING MAIL MANAGER +PLUS+ (MAILCFG.EXE)                   - Page 35 -


           - Log file for FIDO conferences
                 
                 This is an optional argument, and pertains only to sysops who
                 have configured FIDO-style "*.MSG" areas into Mail Manager
                 +Plus+.  If this path/filename is set to anything other than
                 "NONE", Mail Manager +Plus+ will append this text file with
                 the FIDO-style area names of all "*.MSG" conferences that the
                 user uploaded messages to.
                 
                 For instance... if the user uploaded 3 messages to area name
                 "RBBS-PC", two messages to "HS_MODEMS", and 1 message to "FOR-
                 SALE", the resulting log file would be appended with:
                 
                     RBBS-PC
                     HS_MODEMS
                     FOR-SALE
                 
                 Your system's batch files can then take care of any necessary
                 external mail processing based on the contents of this file.
         
           - Door is timelocked from (xx:xx)
                                  to (xx:xx)
                 
                 If you run an echomail system, there may be certain times of
                 the day that you do not want your users into your message
                 bases.  These two arguments tell Mail Manager +Plus+ when to
                 disallow access to the door. To disable, set the "from" and
                 "to" times identically.  For example:  00:00  to  00:00  would
                 let users into the door 24 hours a day.
                 
                 Users with sufficient security to read ALL messages are
                 allowed into the door during the time lock, after receiving a
                 brief warning message.  All other users attempting to access
                 the door during the timelock will be informed that you are
                 processing mail, and will be asked to try again later.
         
           - Allow G)oodbye to drop DTR?
         
                 Either "Y" or "N".  If set to "Y", the door will drop DTR when
                 the user selects G)oodbye from the menu, and also after an
                 E)xpedite! mail session.
                 
                 If set to "N", G)oodbye acts just like Q)uit, and returns the
                 user to the BBS.  E)xpedite! would return the user to the BBS
                 after the user's packet is downloaded.
                 


    CONFIGURING MAIL MANAGER +PLUS+ (MAILCFG.EXE)                   - Page 36 -


                ***************************************************************
                *  WARNING!  - If you have elected to allow the door to drop  *
                *              DTR, do *NOT* have your modem in autoanswer    *
                *  mode!  If you do, it will be possible (although unlikely)  *
                *  for a 2nd user to call and connect in the "window" between *
                *  the door dropping carrier, and when RBBS recovers.  In     *
                *  this case, it is conceivable that this 2nd user could      *
                *  receive a "Welcome back!" message from RBBS, and your      *
                *  board would think that the PREVIOUS user just returned     *
                *  from the door.  As you can see, this could be dangerous.   *
                *  You have been warned!                                      *
                ***************************************************************
         
           - Previous Screen
         
                 Position the cursor over this option, press [ENTER], and you
                 will be taken to the first general configuration screen.
         
           - Edit Conference selections
         
                 Position the cursor over this option, press [ENTER], and you
                 will be taken to the conference selection screen.
           - Exit
         
                 Position the cursor over this option and press [ENTER] (or
                 press [Esc] from anywhere on this screen), and you'll be asked
                 to save your configuration before MAILCFG exits to DOS.
         
         Thus endeth screen #2.


    CONFIGURING MAIL MANAGER +PLUS+ (MAILCFG.EXE)                   - Page 37 -


         ----------------------------------------------------------------------
                         MAILCFG SCREEN #3 - CONFERENCE SELECTION
         ----------------------------------------------------------------------
         
         This screen should look something like this:
         
             1 MAIN       11            21            31            41
             2            12            22            32            42
             3            13            23            33            43
             4            14            24            34            44
             5            15            25            35            45
             6            16            26            36            46
             7            17            27            37            47
             8            18            28            38            48
             9            19            29            39            49
            10            20            30            40            50
         ----------------------------------------------------------------------
         
                             CONFERENCE SELECTION SCREEN
         
                     Use cursor keys to select a conference to edit.
         
                           [ENTER] = Edit this conference.
                            [PgUp] = Move to previous screen.
                            [PgDn] = Move to next screen.
                             [Esc] = Finished editing.
         
         ----------------------------------------------------------------------
         
         You can use the cursor keys, [PgUp], and [PgDn] to switch between all
         of the different conferences possible.  You can configure as many as
         500 conferences.  Position the cursor over the conference that you
         wish to edit, press [ENTER], and you will be taken to the conference
         edit screen.
         
         **********************************************************************
         *  It is VERY IMPORTANT to have your MAIN message area as the first  *
         *  conference listed, and that ALL MAIL MANAGER +PLUS+ USERS have    *
         *  sufficient security to at least READ in this area!  Mail Manager  *
         *  +Plus+ uses this internally for some of it's functions.           *
         **********************************************************************
         
         Press [Esc] (or [PgUp]) when you're finished editing your conferences,
         and you'll be taken back to general configuration screen #2.


    CONFIGURING MAIL MANAGER +PLUS+ (MAILCFG.EXE)                   - Page 38 -


         ----------------------------------------------------------------------
                            MAILCFG SCREEN #4 - CONFERENCE EDIT
         ----------------------------------------------------------------------
         
         Once you've pressed [ENTER] at the conference selection screen, up
         will pop something that looks like this:
         
                                    Editing Conference #1
             Conference name .............................: MAIN
             Conference description ......................: Main message base
             FIDO area name ..............................: N/A
             Message base type: Y=Fixed, N=Elastic, F=Fido: N
             Path/Name of conference USERS file:
                  C:\RBBS\MAINU.DEF
             Path/Name of conference MESSAGES file:
                  C:\RBBS\MAINM.DEF
             Allow ANSI graphics in uploaded messages? ...: Y
             Allow high & low ASCII in uploaded messages? : Y
             Security level to READ this conference ......: 5
             Security level to POST in this conference ...: 5
             Tagline for this conference:                        Add tag: N/A
                  NONE
             Use Fido-style tearlines? ...................: N       Zone: N/A
             Allow users to join within Mail Manager? ....: N        Net: N/A
             Maximum # of lines per message ..............: 99      Node: N/A
             Path/Name of conference ALIAS file:                 Netmail: N/A
                  NONE
         
           Press [Esc] or [F10] when finished with the conference.
         ----------------------------------------------------------------------
         
         Several of these options pertain only to FIDO *.MSG areas, and some
         have different meaning to FIDO *.MSG areas.  We will attempt to cover
         each one individually as completely as possible:
         
           - Conference Name
         
                 Up to 7 characters that you will use to describe this
                 conference to the users.  Normally set as the first 7
                 characters of the name of the MESSAGES and USERS file,
                 although you can put anything in here.  For FIDO *.MSG areas,
                 you will want to match this as closely as possible to the true
                 FIDO-style area name of the conference, since this is what
                 will be displayed to the users.
                 
                 The important thing is to describe the conference as fully as
                 possible (for the users) in the 7 characters that you have
                 available.  The 25-character conference description will
                 describe it for them a lot better.
                 
                 If the conference name is left blank, or it is set to
                 "{EMPTY}", pressing [F10] will cause MAILCFG to ask you
                 whether or not to reserve a space for this conference number.
                 If you do NOT reserve the space, this conference number will
                 be skipped when you save your settings.


    CONFIGURING MAIL MANAGER +PLUS+ (MAILCFG.EXE)                   - Page 39 -


           - Conference description
         
                 Up to 25 characters that you will use to more fully describe
                 the
                 conference to the users.  This field will be (optionally)
                 shown
                 to the users when they are configuring which conferences to
                 follow
                 within the door, and also when selecting which conferences to
                 R)ead or P)ost a message in.
                 
                 If the user is in expert mode, the default is to NOT show them
                 the
                 conference description.  If in novice mode (display the
                 menus),
                 the default is to show conference descriptions.  The user is
                 given
                 a choice at all times.
                 
                 When displaying conference descriptions, the user will see 15
                 conferences on each screen.  When NOT displaying descriptions,
                 the user will see 50 conferences per screen.
                 
           - FIDO area name
         
                 Pertains only to FIDO *.MSG areas, and optional.  If not a
                 FIDO *.MSG area, this field will be skipped.
                 
                 This should be set to the exact FIDO-style area name of the
                 conference, as your external mail processor knows it.  This
                 name is used ONLY when appending the optional log file, as set
                 in the general configuration.
         
           - Path/Name of conference USERS file
         
                 Full path to your RBBS-PC users file for this conference.
                 
                 A quick note here:  You really should have a unique USERS file
                 for each conference/subboard.  RBBS-PC does not absolutely
                 require this, but it is necessary to keep the last message
                 read
                 in each conference updated, and for Mail Manager to know
                 exactly
                 which messages to extract and prepare to download for the
                 users.
                 
                 If this is a FIDO *.MSG area, this setting has no meaning to
                 Mail Manager +Plus+, and you can literally put whatever you
                 want in here in this case.
         


    CONFIGURING MAIL MANAGER +PLUS+ (MAILCFG.EXE)                   - Page 40 -


           - Path/Name of conference MESSAGES file
         
                 Full path to your RBBS-PC messages file for this conference.
                 
                 If this is a FIDO *.MSG area, this must be set to the full
                 pathname to this area's *.MSG's.  The trailing backslash is
                 optional.  For example, if set to:
                 
                    C:\MAIL\4SALE
                 
                 Mail Manager +Plus+ will manipulate files named:
                 
                    C:\MAIL\4SALE\*.*
                 
         
           - Allow ANSI graphics in uploaded messages?
         
                 "Y" or "N".  If set to "N", Mail Manager will strip all escape
                 characters out of uploaded messages, effectively disabling
                 ANSI.
         
           - Allow high & low ASCII in uploaded messages?
                 
                 "Y" or "N".  If set to "N", Mail Manager will strip all high
                 and low ascii characters out of uploaded messages, replacing
                 them by either blank spaces, or an equivalent "normal"
                 character.
                 
                 The most common reason for disabling both ANSI and ASCII is to
                 conform to FIDO-NET rules & regs, although there are several
                 reasons why you might want to disable ANSI.
         
           - Security level to READ this conference
         
                 Minimum security level required to see this conference listed
                 in Mail Manager's configuration menu.  If the user does not
                 have sufficient security to READ this conference, the
                 conference name will be replaced by " --- " in Mail Manager's
                 menu, and the user will not be allowed to download messages
                 (or upload replies) in this conference.
         
           - Security level to POST in this conference
         
                 Minimum security level required to leave a message in this
                 conference.  If the user's security level is lower than this,
                 yet the same as (or higher than) the security required to
                 READ, any messages that he/she uploads to this conference will
                 result in the following:
         
                 þ A Mail Manager security violation notice being passed back
                   to the user in the MAIN area, as a private message.  This
                   message will be shown as being from "MAIL MANAGER".
                 þ The uploaded message itself being ignored.  Nothing will be
                   posted in the conference.
                 


    CONFIGURING MAIL MANAGER +PLUS+ (MAILCFG.EXE)                   - Page 41 -


           - Tagline for this conference
         
                 The tagline that you want to use for this particular
                 conference.  If set to "NONE", Mail Manager will use the
                 default tagline.  If the default tagline is also "NONE", no
                 tagline will be appended to the end of the message.
                 
                 If this is a FIDO *.MSG area, this is the tagline that will be
                 posted to the message if tear/taglines are turned on.
         
           - Use FIDO-style tearlines?
         
                 During our development of Mail Manager and Mail Manager
                 +Plus+, there was much discussion to and fro in the various
                 echos regarding the allowability of mail reader tearlines "---
                 ".  At this writing, it is not clear as to whether or not
                 these additional tearlines on echo messages will be
                 permissible.  In any case, we gave you an out.  Set this to
                 "Y", and any mail reader tearlines on uploaded messages will
                 be replaced by three blank spaces.  Set to "N", and they will
                 be passed into the message untouched.
         
           - Type of msg base: Y=Fixed, N=Elastic, F=Fido?
         
                 VERY IMPORTANT, and either "Y", "N", or "F".  RBBS-PC and Mail
                 Manager +Plus+ handle fixed-length conferences differently
                 from those that are configured to "grow" as messages are
                 added.
                 
                 If set to "F", you are telling Mail Manager +Plus+ that this
                 is a FIDO *.MSG area, and all of the "N/A"'s that you see on
                 this screen will be replaced by the current settings.  You
                 will also be allowed to edit the options specific to FIDO
                 *.MSG areas.
                 
                 Setting this option to "Y" or "N" turns "off" all of the FIDO-
                 specific options, and replaces their values with "N/A".  All
                 of the FIDO-specific options will be unavailable for edit.
         
           - Allow users to join within Mail Manager?
         
                 Either "Y" or "N".  (Has no meaning to FIDO *.MSG areas)
                 
                 If set to "Y", Mail Manager +Plus+ will allow your users to
                 automatically "join" this conference when they attempt to flag
                 it as active, and add them to the conference user file if they
                 have not joined it from the BBS.
                 
                 If set to "N", the user will have to use the J)oin command in
                 RBBS-PC to become a member of the conference.
                 
                 FIDO *.MSG areas cannot be joined from within RBBS-PC, and
                 can therefore always be "auto-joined" from within Mail Manager
                 +Plus+, regardless of this setting.
         


    CONFIGURING MAIL MANAGER +PLUS+ (MAILCFG.EXE)                   - Page 42 -


           - Maximum # of lines per message
         
                 Default = 99.  You can select any number of lines per message
                 that you desire for this conference, from 9 to 99, or 0 if you
                 don't care how long the uploaded messages are.  When the user
                 attempts to post a message from within a REP packet, the door
                 will, if necessary, "split" long messages into several smaller
                 ones which will fit within this line limit.
                 
                 **************************************************************
                 *  Note that messages from normal users will be limited to 8 *
                 *  lines less than this setting, while network packets from  *
                 *  "net-status" user names will be able to utilize the full  *
                 *  line limit prior to being split.                          *
                 **************************************************************
                 
                 The door will also use this number when the user attempts to
                 R)ead, reply, or P)ost a message online, and will not allow
                 the number of lines to exceed what you specify here.  If "0",
                 99 lines per message are allowed in R)ead/P)ost online.
         
           - Path/Name of conference ALIAS file
         
                 There is a popular merge available for RBBS-PC that allows the
                 use of alias names.  If you are not using the ALIAS merge, you
                 can still make use of this option, if you would like a few
                 users to be able to post messages under a different name than
                 the one they use on the BBS.  Set this option to "NONE" if you
                 are not using alias names.
                 
                 Since alias names are taboo in the Fido kingdom, this setting
                 is ignored for Fido *.MSG areas.
                 
                 The filename that this option points to is a text file,
                 formatted as follows:
                 
                    REAL NAME, ALIAS NAME
                 
                 So, to have all messages uploaded by "JOE DOE" posted as being
                 from "MAIL ADDICT", and to have the SysOp's own messages
                 posted as being from "TEST SYSOPNAME", this file would look
                 like this:
                 
                    JOE DOE, MAIL ADDICT
                    REMOTE NAME, TEST SYSOPNAME
                 
                 "REMOTE NAME" would of course be replaced by the name that you
                 use to sign onto your system remotely.
                 
                 Mail Manager +Plus+ is smart enough to take care of updating
                 the mail waiting flag in RBBS-PC for the REAL NAME of the
                 recipient, and to add messages addressed to the user's alias
                 to the personal index of the recipient's mail packets.
         


    CONFIGURING MAIL MANAGER +PLUS+ (MAILCFG.EXE)                   - Page 43 -


           - Add tag
         
                 Applies to FIDO *.MSG areas only.
                 
                 If set to "Y", Mail Manager +Plus+ will append a tear and
                 origin line to messages uploaded to this conference, such as:
                 
                    --- MMGR+ v3.10
                     * Origin: [Tagline for this conference] (Zone:Net/Node)
                 
                 If set to "N", the tear/tag is *NOT* appended to the uploaded
                 messages.  (Normally, this is a function of your mail
                 processor, but you may want Mail Manager +Plus+ to append
                 these lines in your NETMAIL areas).
         
           - Zone
         
                 Applies to FIDO *.MSG areas only.
                 
                 FIDO-NET is normally "1", RBBS-NET is normally "8".  Each
                 conference can be set to different Zone:Net/Node arguments, so
                 Mail Manager +Plus+ allows you to be in MANY different mail
                 zones!
         
           - Net
         
                 As above, applies to FIDO *.MSG areas only.
                 
                 Set this to the net number you are using for this conference.
                 
           - Node
         
                 As above, applies to FIDO *.MSG areas only.
                 
                 Set this to the node number you are using for this conference.
                 For these three options, settings of:
                 
                    Zone: 8
                     Net: 965
                    Node: 9
                 
                 ...would mean a FIDO-style address of "8:965/9".
         


    CONFIGURING MAIL MANAGER +PLUS+ (MAILCFG.EXE)                   - Page 44 -


           - Netmail
         
                 Applies to FIDO *.MSG areas only.
                 
                 THIS IS A VERY IMPORTANT SETTING.  If this is a netmail area,
                 set it to "Y", otherwise DEFINITELY set it to "N"!  Mail
                 Manager +Plus+ handles netmail areas quite differently than
                 standard *.MSG echo areas, and messages will *NOT* be posted
                 properly if this setting is incorrect.
                 
                 Please see the section of this document regarding FIDO *.MSG
                 areas for all the info on Mail Manager +Plus+'s handling of
                 netmail areas.


    CONFIGURING MAIL MANAGER +PLUS+ (MAILCFG.EXE)                   - Page 45 -


         MULTIPLE CONFIGURATION FILES
         ----------------------------
         
         When Mail Manager +Plus+ loads, it will first look for a node-specific
         configuration file MAILCFGx.CFG (where x would be the node number).
         If no node-specific configuration file is found, Mail Manager then
         defaults back to MAILMGR.CFG.  This permits you to have a separate
         configuration file for any node that requires one.
         
         To edit a configuration file other than the default MAILMGR.CFG, enter
         the filename on the MAILCFG command line.  For instance, to edit
         MAILMGR2.CFG, your command might be:
         
            MAILCFG C:\MAILMGR\MAILMGR2.CFG
         
         MAILCFG will look for and edit the filename MAILMGR.CFG (in the
         current directory) if nothing is passed on the command line.
         
         Please be aware that Mail Manager +Plus+ can use the same
         configuration file between the various nodes of your RBBS-PC, and file
         sharing/locking is fully implemented.  Therefore it is not necessary
         to create multiple configuration files unless you have unique
         requirements between nodes.  (Non-standard port configurations is one
         example, where you may want to have different MAILMGR.PRO files.
         Since the path/name of MAILMGR.PRO is specified in the configuration
         file, this would make for a good argument to use multiple
         configuration files).


    FIDO-STYLE *.MSG MESSAGE AREAS                                  - Page 46 -


         AN INTRODUCTION TO FIDO FORMAT
         ------------------------------
         
         If you do not wish to use FIDO-style *.MSG formatted conferences with
         Mail Manager +PLUS+, you may skip this section.
         
         Mail Manager +PLUS+ merely allows you to access FIDO-style message
         bases via an offline mail door, it does not handle the actual
         transmission or reception of these messages.  For that you need a
         separate frontend mailer such as BinkleyTerm or Front Door.
         
         Mail Manager's handling of FIDO conferences is MUCH slower than its
         handling of RBBS conferences.  You may seriously wish to consider
         tossing FIDO conferences into standard RBBS message bases in order to
         speed up Mail Manager operation.  Utilities from other authors for
         doing this include RBBSMail, MsgToss, and OverMail.  The time spent
         doing this ONCE for each mail packet received may amount to
         considerable time savings for EACH time a caller uses this door.
         
         Before we talk about the intricacies of setting up Mail Manager +Plus+
         with your FIDO-style system, we should talk about this particular
         format for a bit.
         
         RBBS-PC is capable of running under a frontend mailer such as Binkley-
         Term, Frontdoor, Seadog, etc. etc.  Depending on what type of mail
         processor the Sysop is using, mail can normally be "tossed" into
         either RBBS-PC message bases, or into the native FIDO-NET format,
         which is termed here as "*.MSG".  Some Sysops prefer to keep their
         echo mail in FIDO format, rather than converting all incoming and
         outgoing messages to and from RBBS-PC *M.DEF's.
         
         FIDO "message bases" consist of a unique DOS subdirectory for every
         conference, with each message i a separate file.  A DOS directory
         structure for this type of message format will typically look
         something like this:
         
               C:\FIDO        (Base mail directory)
               C:\FIDO\4SALE  (First conference)
               C:\FIDO\RBBS   (Second conference)
               ...            ...so on and so forth.
         
         Within each directory (or "conference") will be filenames like 1.MSG,
         2.MSG, 3.MSG, etc. etc.  The first message in each conference (1.MSG)
         is normally some type of "checkpoint" file for mail processors (such
         as QM, et al), and is therefore not usually available for reading by
         the user.  An exception to this is any "NETMAIL" area that the sysop
         has set up.  Netmail conferences do not go through quite the same
         process as regular echo conferences do, and in these types of areas,
         1.MSG is usually permissible reading material.
         
         But let's not get ahead of ourselves, here.  We'll come back to
         handling netmail later.
         


    FIDO-STYLE *.MSG MESSAGE AREAS                                  - Page 47 -


         Setting up FIDO conferences in Mail Manager is a fairly
         straightforward process, but there are several things that you will
         need to keep in mind:
         
             - FIDO conferences don't have a user file for Mail Manager +Plus+
               to rely on.  Therefore, Mail Manager +Plus+ creates one for
               itself in each FIDO area, named "MMGR.USR".
             
             - FIDO conferences don't have any built-in indexing available,
               short of reading each and every message every time the
               conference is accessed.  Therefore, Mail Manager +Plus+ creates
               one for itself in each FIDO area, named "MMGR.NDX".
             
             - FIDO conferences cannot be joined from within RBBS-PC.
               Therefore, Mail Manager +Plus+ will allow every user with
               sufficient security to read the conference to "join"
               transparently from within the door.
             
             - FIDO conferences are usually renumbered every night.  This means
               that what was message number 175 on one day might become message
               number 37 on the next.  Mail Manager therefore determines a
               unique CRC for each message, based on selected unchanging
               portions of each message header.  This information is stored in
               the "MMGR.NDX" file within each conference.
             
             - This index should be updated right after your
               renumbering/maintenance event, to save the first hapless user a
               *LOT* of time while Mail Manager +Plus+ re-creates it.  That's
               what the supplied MMINDEX.EXE program is for, and we'll get into
               the usage of this program shortly.
             
             - Mail Manager must know your Zone:Net/Node ID for each FIDO
               conference, so that it can properly create the message headers
               of all uploaded replies to these areas.
             
         SETTING UP YOUR FIRST FIDO *.MSG AREA
         -------------------------------------
         
         With all that in mind, try setting up your first FIDO conference in
         Mail Manager +Plus+.  Make sure that it is working properly before you
         add the entire slew of conferences!  At MAILCFG's conference edit
         screen, there are several options unique to FIDO conferences that are
         worthy of note:
         
             Path/Name of conference USERS file ..:  Ignored by Mail Manager
               for FIDO conferences.  You can literally put whatever you want
               in this field.
             
             Path/Name of conference MESSAGES file:  This is the DOS PATH to
               the conference, rather than the name of the *M.DEF file.  For
               instance, if you enter "C:\MAIL\4SALE", Mail Manager will
               manipulate files named
               
                     "C:\MAIL\4SALE\*.*".  A trailing backslash is optional.
             


    FIDO-STYLE *.MSG MESSAGE AREAS                                  - Page 48 -


             Allow ANSI graphics in uploaded messages? : NO.  FIDO-NET doesn't
               like ANSI.
             
             Allow high & low ASCII .................. : NO.  Moderators will
               be all over you if they find messages containing high ASCII that
               originated on your system.
             
             Use FIDO-STYLE tearlines? ............... : YES.  This strips out
               the "---" tearlines that offline readers like to stick on
               uploaded messages.  Your FIDO-NET mail processor will add a
               tearline and tag of its own, and duplicate tearlines are taboo
               in the FIDO kingdom.
             
             Message base type: Y=Fixed, N=Elastic, F=FIDO: F
             
             Allow users to join within Mail Manager? ....: Ignored by Mail
               Manager +Plus+ for FIDO areas.  Any user with sufficient
               security to READ the conference can "join" from within the door.
             
             Path/Name of conference ALIAS file? .........: Aliases aren't much
               good in FIDO land, either.  This setting is ignored for FIDO
               conferences.  (See the section regarding "CONFIGURING MAIL
               MANAGER +PLUS+" for more information regarding alias names).
             
             Zone:  Set to your mail zone (U.S. FIDO-NET would be 1).
             Net:   Set to your net ID (HOTLine's FIDO-NET net ID is 380).
             Node:  Set to your node ID (HOTLine's FIDO-NET node is 14).
             
               (These examples would mean an address of 1:380/14).
             
             Netmail:  VERY IMPORTANT.  If you are configuring a netmail
               conference, set this option to "Y".  Otherwise, DEFINITELY set
               it to "N"!
         
         Now save your configuration, and as far as Mail Manager +Plus+ is
         concerned, you just added a FIDO conference.
         
         BEFORE YOU EXTRACT MAIL FROM THE CONFERENCE, be sure that there is a
         file named "1.MSG" in that directory.  Results can be unpredictable if
         Mail Manager +Plus+ sees only "2.MSG" and up.  Also, remember that
         there is no Mail Manager +Plus+ index created as of yet.  You'll want
         to run the MMINDEX.EXE program to initialize the conference for Mail
         Manager +Plus+'s use.  Although this last is not TRULY necessary, it
         will speed up initial operation for that conference considerably,
         especially if it contains a few hundred messages or so.  Usage for
         MMINDEX:
         
             MMINDEX D:\PATH\MAILMGR.CFG
         
         If no filename is passed on the command line, MMINDEX will look for
         MAILMGR.CFG in the current directory.  MMINDEX reads your Mail Manager
         +Plus+ configuration file, and creates an index file in all of your
         FIDO conferences.
         


    FIDO-STYLE *.MSG MESSAGE AREAS                                  - Page 49 -


         At this point, you're ready to test out the conference from within
         Mail Manager +Plus+ itself.  When satisfied, you can do one of two
         things:
         
            1) Go back to MailCFG and repeat all but the MMINDEX.EXE step for
               the rest of your FIDO confs.  Or,
            
            2) Run the supplied CFG2TXT utility against your MAILMGR.CFG.  This
               will create a text file that you can use your favorite text
               editor against, and add the balance of your FIDO conferences.
               When finished, run the companion program, TXT2CFG to convert the
               text file back into Mail Manager +Plus+'s binary configuration
               format.  If you have MANY Fido conferences to configure, this
               might be the way to go.
            
            See the section of this document regarding "UTILITY PROGRAMS" for
            more information on these two utilities.
         
         After doing one of these two things, run MMINDEX.EXE as the very last
         item BEFORE firing Mail Manager +Plus+ back up for more testing.
         Remember to add it to your nightly event, as the very LAST thing run
         before your BBS comes back up.
         


    FIDO-STYLE *.MSG MESSAGE AREAS                                  - Page 50 -


         NETMAIL CONFERENCES
         -------------------
         
         Guess what!  Netmail areas require a little more work.  "Regular"
         echomail *.MSG areas are scanned out by your mail processor for
         sending to your host.  NETMAIL, on the other hand, can be sent
         anywhere, either directly from your system to destination, or routed
         through your HOST.
         
         The most courteous way to do this is generally thought to be via
         "Crash" or "Direct" netmail, which bypasses the network and puts you
         in immediate contact with the individual system.  By going direct,
         there are other fun things that are considered almost automatic for
         Sysops of frontend mailer systems, such as "File Attach", and "File
         Request" (commonly referred to as "FREQ"), not to mention that non-
         involved parties shouldn't have to front the long distance bill for
         personal messages between two individuals in the net.
         
         On the other hand, if you're sending mail to your host, you might want
         to send the message normally, which means that it would be sent out
         when your mail packer picks it up during your regular mail event.
         This way, you don't have to make two separate (and possibly long-
         distance) calls to your host if you want to send them netmail.
         
         In any case... you need to inform Mail Manager of your outbound
         directories for NETMAIL zones.  In most cases, you will have a
         separate outbound directory for each mail zone.  There are a number of
         ways to go about this from the standpoint of your frontend mailer, but
         the important thing is that as the SysOp of the board, you should
         already know where they are!
         
         Create a file named MMGRNODE.OB in your Mail Manager Directory.  This
         is a simple text file, and does nothing more than inform Mail Manager
         where to put File requests, File attaches, and outbound netmail when
         creating a CRASH message.  The format for each line is:  Zone,
         X:\PATH\OUTBOUND.DIR  So, if you are in 3 different mail zones, your
         MMGRNODE.OB file would look something like this:
         
              1, C:\BINKLEY\OUTBOUND
              8, C:\BINKLEY\OUTBOUND.008
              10, C:\BINKLEY\OUTBOUND.010
         
         ...and that's all that's needed for your MMGRNODE.OB text file.
         
         If you are in more than one mail network, you may be using what are
         termed as "AKA" addresses.  In this case, the Zone:Net/Node address
         that you configured for this netmail area may not always be what you
         want Mail Manager +Plus+ to use.  For instance, if you are a member of
         both Rbbsnet and FidoNet, you may wish to send a message to someone
         that is reachable only through RBBSNet in zone 8.  In this case, you
         may want the recipient of the message to see your RBBSNet address on
         the message, rather than your Fido address.
         


    FIDO-STYLE *.MSG MESSAGE AREAS                                  - Page 51 -


         Our solution to this is a file named MMGRNODE.AKA, which Mail Manager
         +Plus+ will look for in your Mail Manager +Plus+ directory.  This text
         file is formatted as such for each line:   Zone:Net/Node   So, to copy
         the above-mentioned example, your MMGRNODE.AKA file might look like:
         
             1:226/1400
             8:965/9
             10:10/1
         
         See the section of this document entitled "Text files for FIDO netmail
         areas" for the full scoop on MMGRNODE.OB and MMGRNODE.AKA.
         
         NOW, we have to get into something that we're probably going to catch
         flak about, and that's our implementation of how to handle searching
         the nodelist to find the system to which you're sending netmail
         messages.
         
         Mail Manager +Plus+ uses a proprietary nodelist format.  It just is
         not feasible at this stage of the game for us to attempt to support
         Version 6 and/or Version 7 nodelists, so we deemed it best to use a
         format of our own, optimized for FAST searches and small file size.
         You need not use our implementation of the nodelist, but if you don't,
         you will lose convenience, and will then need to be able to enter in
         the exact Zone, Net, and Node ID of the recipient on every netmail
         message, with no search options.
         
         MMGRNODE.EXE is Mail Manager +Plus+'s proprietary nodelist compiler.
         This executable should be placed in your Mail Manager +Plus+
         directory, and should be run whenever you update your nodelists.  Its
         usage is:
         
               MMGRNODE [/A] X:\PATH\NODELIST.FIL
                  
                  /A  - Tells Mail Manager +Plus+ to append to the existing
                        compiled nodelist.  If omitted, Mail Manager +Plus+
                        will create the compiled nodelist from scratch,
                        overwriting any pre-existing one. (By "Compiled
                        nodelist", we are referring to Mail Manager +Plus+'s
                        proprietary one, MMGRNODE.DAT).
                  
                  X:\PATH\NODELIST.FIL - The path/filename to the raw nodelist
                        that you are compiling.
         
         MMGRNODE will create two files in the current DOS subdirectory:
         
                  MMGRNODE.DAT - The main data file containing Sysop names,
                        Zone, Net, and node numbers, and phone numbers.  All
                        other information in the raw nodelist is ignored, to
                        save on file size as much as possible.
                  
                  MMGRNODE.DIX - The data file's index.  This file will be MUCH
                        smaller, and contains information to quickly jump to an
                        individual system's info based on Zone, Net, and Node.
         


    FIDO-STYLE *.MSG MESSAGE AREAS                                  - Page 52 -


         Mail Manager +Plus+ will look for these two files in your Mail Manager
         directory whenever a netmail message is found within a reply packet.
         
         For those using multiple nodelists, consider which one you'll use the
         most, and compile that one FIRST, to improve on search speed.  For
         example, say you're compiling the RBBS-NET nodelist (zone 8) and the
         entire FIDO-NET nodelist.  RBBSLIST is so small that the search time
         to go through it to get to FIDO addresses is minimal.  On the other
         hand, it would take considerably longer to have to go through the
         entire FIDONET nodelist when you're looking for someone in RBBS-NET.
         You get the idea.  To compile using this scenario, here's the command
         lines you'd use (we'll just use dummy nodelist filenames for the
         moment).  Make sure you're in your Mail Manager +Plus+ directory!:
         
           MMGRNODE C:\BINKLEY\RBBSLIST.178
           MMGRNODE /A C:\BINKLEY\NODELIST.094
         
         This would create MMGRNODE.DAT and MMGRNODE.DIX from scratch, starting
         with the RBBS-NET nodelist.  The FIDO nodelist would be appended to
         it.  You can append as many nodelists as you'd like in this way.  (We
         tried five, for testing purposes, and had no trouble).
         
         At this point, you should be all setup and ready to roll with your
         FIDO areas, as well as your NETMAIL areas.


    FIDO-STYLE *.MSG MESSAGE AREAS                                  - Page 53 -


         NETMAIL MESSAGES WITHIN REPLY PACKETS
         -------------------------------------
         
         Uploaded *.REP's will work just like they always have within Mail
         Manager and Mail Manager +Plus+, until you run into a NETMAIL message.
         When Mail Manager +Plus+ encounters a message for a conference you
         have configured as netmail in your REP packet, it stops to ask you a
         few questions, so DON'T RUN MAIL MANAGER +PLUS+ FROM A SCRIPT, IF
         YOU'RE UPLOADING NETMAIL!  There *is* one exception to this rule:
         read on to find out what it is.
         
         You'll be informed that this is a *NETMAIL MESSAGE*, then will be
         asked a series of questions:
         
         Users that have sufficient security to read ALL messages (or higher)
         will get the option of posting the message as C)rash, and will also
         get the file request and attach options.  Users with security LOWER
         than this will not get these options, and their netmail will be posted
         "normally" (as an *.MSG in your netmail directory, waiting to be
         tossed out by your mail processor).
         
         If the user has sufficient security, the first question will be:
         "Send message [N]ormally, or C)rash?"
         
            (Defaults to normal).  A crash message goes directly to your
            outbound area, and is also posted (and marked as sent) in your
            netmail area.  A normal message is posted in your netmail area, and
            is not sent to anyone until your mail packer finds and moves it.
         
         If a (C)rash message, you'll be asked: "File attach Y/[N]?"
         
            (Defaults to No).  If you tell it yes, you'll be prompted for the
            path/filename to send out.
         
         If a (C)rash message, you'll also be asked: "File request Y/[N]?"
            
            (Defaults to No).  If you tell it yes, you'll be prompted for the
            name to request.
            
            NOTE - In our current state of development, you can do one or the
            other (attach or request), but not both!  If you really need to
            both attach and request to the same system at the same time, you'll
            have to upload two separate netmail messages:  1 for the request,
            and 1 for the attach.
         
         "Private Message Y/N?"
         
            Defaults to whatever it was set to in the REP packet.
         


    FIDO-STYLE *.MSG MESSAGE AREAS                                  - Page 54 -


         "Search by I)D, or S)ysop name ([ENTER] = bypass the search)?"
         
            This is where Mail Manager +Plus+ will look at the MMGRNODE.DAT and
            MMGRNODE.DIX files created by the MMGRNODE.EXE nodelist compiler.
            Here are what the 3 options mean to you:
            
            (I)D - You'll be asked for an exact Zone, Net, and then Node number
                 to look up.  If Mail Manager +Plus+ finds a hit, it will first
                 ask you whether or not to [A]ccept what it found, then either
                 search again, or ask you whether or not to post the message.
                 The ID search uses the data index file, and is VERY fast.
            
            (S)ysop name - You'll be asked for a partial sysop name to look
                 for.  The search is NOT case sensitive.  As soon as Mail
                 Manager +Plus+ finds the first hit, it displays what it finds,
                 and asks you whether to accept what it found, or search again.
            
            [ENTER] - Bypass the search.  You'll key in the Zone, net and node
                 ID's, and *NO* error checking will be performed.  Mail Manager
                 will take whatever you give it, and attempt to post the
                 message.  This is the only option available to you if you did
                 not utilize the MMGRNODE.EXE program.
            
            Post Message Y)es, N)o, M)odify ([ENTER] = Y)?
            
         We do give you one last chance to abort the message <grin>.  If you
         made a mistake, you can choose "M" to start over and re-enter the
         information.
         
         There is a quick and easy way to bypass all of this.  If the very
         first line of the message body contains nothing but "TO: address",
         then the door will attempt to use that address as a normal message (to
         be scanned out later by your mail processor).  For example, if the
         first line of the message body reads:
                                 TO: 1:380/14
         ...here is what will happen:
         
             - MMGRNODE.NDX is searched for Zone 1, and Net 380.
             
             - If found, MMGRNODE.DAT is searched for 1:380/14.
             
             - If found, the message will be posted normally in your netmail
               area, without requiring further intervention.
             
             If any of the above are NOT found, the "TO:" line is ignored, and
             you will be prompted as always for the full information about the
             netmail message.
         
         This works for netmail messages found within REP packets, as well as
         netmail messages that are entered online within the door.
         
         You cannot send a CRASH message or a file attach/request in this way,
         but you might find this option handy for posting a quickie routed
         message now and then.


    FIDO-STYLE *.MSG MESSAGE AREAS                                  - Page 55 -


         LAST MINUTE THOUGHTS ON FIDO
         ----------------------------
         
         That's about it for the FIDO *.MSG and NETMAIL implementations.  A
         couple of things that should probably be mentioned:  Eddie Rowe has
         written a program that we have never tried, and that's NoSnail.
         NoSnail has the capability of sending netmail from an RBBS-PC message
         base (*M.DEF).  If you are using this utility, you can ignore all of
         the above for netmail areas, and use Eddie's instructions instead.
         
         Message extracting, and manually setting last message read markers are
         noticeably slower in *.MSG conferences.  There are several reasons for
         this, most of which probably don't need a lot of explanation, but here
         are a few anyway:
         
         Each message is in a separate file.  Therefore, there's an awful lot
         of file opening and closing going on.
         
         A user might be posting (or have just posted) a FIDO message via Mail
         Manager (or some other utility) on another node of your BBS.  We
         perform checks to guard against this (and allow for it), which slows
         things down a bit.
         
         Fido messages don't have a whole lot of "standardization".  A
         perfectly valid message could have any number of different things
         determining end of printable line, or *NO* end of line markers at all.
         So, there's a lot of checking and conversion to be done in order to
         get the message into QWK format.
         
         Beyond that... it is acceptably fast on a non-networked system (even a
         fairly slow one), but the extraction process really bogs down when run
         through a network with fairly slow transfer rates.  We are working on
         a few ideas to speed up the extraction process in some future release.


    MISCELLANEOUS CONSIDERATIONS                                    - Page 56 -


         DEBUGGING YOUR SETUP, AND RUNNING IN LOCAL MODE
         -----------------------------------------------
         
         Assuming (again) that your Mail Manager +Plus+ directory is named
         \MAILMGR:
         
         Change to the \MAILMGR directory, and run MAILMGR.EXE with no
         command line to bring the door up in local mode.
         
         NOTE - Depending on how many conferences you've entered, Mail Manager
         +Plus+ may take a while to come up.  Mail Manager +Plus+ attempts to
         find the user in each and every conference as soon as it loads to
         determine which conferences the user has and has not joined.  The more
         conferences you have, and the slower your hard disk, the longer this
         will take.  This is required by the security measures mentioned in the
         'features' section.
         
         If this is a first-time installation, Mail Manager +Plus+ should say
         that you're a new user and walk you through the user setup.
         
         We think it is necessary to mention Mail Manager +Plus+'s own running
         scenario, since it is important for you as the SysOp to understand
         this for any debugging purposes on your end.
         
         You created   +-- Work directories created & maintained by the door.
                |      |
            \MAILMGR   |
                       |
            \MAILMGR\LOCAL
                    \NODE1
                    \NODE2
                    ...etc.
         
         Mail Manager +Plus+ changes to these work directories as it runs, and
         changes back to the parent directory just as it exits.  If you used
         the "/W" work directory command line switch, these directories will be
         created and manipulated wherever you specified them to be.
         
         If you are not using Mail Manager's list of archivers (MAILMGR.ARL),
         one file that absolutely MUST be in the directory that you created is
         RBBSQWK.BAT.   If you are running the list of archivers, this file is
         not needed.
         
         For those NOT running MAILMGR.ARL:  DON'T RENAME RBBSQWK.BAT!!!
         
         You can edit RBBSQWK.BAT if you are familiar with the format of the
         CONTROL.DAT file that is included in all .QWK packets, and/or want to
         modify what the users will receive in their QWK's.  This is not for
         the faint of heart, requires some knowledge of how things work in QWK
         land, and simply isn't necessary.  RBBSQWK.BAT is run each time that
         Mail Manager +Plus+ creates a QWK packet for the user to download, and
         doesn't do anything at all if you are using the list of archivers,
         MAILMGR.ARL.
         


    MISCELLANEOUS CONSIDERATIONS                                    - Page 57 -


         FOR A FIRST-TIME INSTALLATION, WE RECOMMEND YOU DON'T MODIFY
         RBBSQWK.BAT!
         
         An important consideration is what to do with your own personal QWK's
         and REP's created locally.  You may find it convenient to configure
         your offline reader to use the \MAILMGR\LOCAL directory for all .REP's
         and .QWK's, since that's where Mail Manager will manipulate your mail
         in local mode.
         
         To stick a .REP packet into your message bases, just U)pload while in
         local mode, and select any protocol other than N)one.  If your .REP
         packet is in the \MAILMGR\LOCAL directory, it will be processed as if
         you'd uploaded the file remotely.
         
         It is important to make you aware that there is a sysop-only menu
         option available, and that's "I" (Info), which isn't listed in either
         the command prompt, or the menu itself.  This menu option is available
         only to those with sufficient security to read ALL messages, or
         greater.  If the user does not have at least this security level, they
         will see the familiar "Command not recognized", instead.
         
         If you have set yourself up with sufficient security to use this
         option, pressing "I" at the Mail Manager +Plus+ main menu will greet
         you with something like this:
         
               SYSOP INFORMATION:
         
               Mail Manager version ............: v3.10
               Mail Manager path ...............: C:\MAILMGR
               MailMGR's operating environment .: LANtastic v4.10 (NetBIOS)
               DOS version .....................: 6.00
               DOS SHARE detected? .............: Yes
               Flow control method .............: Local mode
               Free string space ...............: 20624
               Non-string array avail ..........: 273408
               Available stack space ...........: 1738
               MAIN message base ...............: E:\RBBS\MAINM.DEF
               MAIN users file .................: E:\RBBS\MAINU.DEF
               Highest message # in MAIN .......: 6132
               Last msg # YOU read in MAIN .....: 6131
               Filename of protocol definitions : C:\MAILMGR\MAILMGR.PRO
               Filename of list of archivers ...: C:\MAILMGR\MAILMGR.ARL
               Filename of FMS directory .......: E:\RBBS\MASTER.DIR
               RBBS-PC semaphore file ..........: E:\RBBS\IBMFLAGS
               MailMGR semaphore file ..........: MMFLAGS
               RBBS-PC semaphore file size (6) .: 6
               MailMGR semaphore size (3) .: 3
         
            These 20 are all of the possible lines that can be shown to you.
            The last four will be displayed only if your environment is
            NetBIOS.
         


    MISCELLANEOUS CONSIDERATIONS                                    - Page 58 -


            Some of the more important information in here:
         
               Mail Manager path should reflect the drive and directory that
               you have installed the program in.  If it doesn't, your batch
               file is probably not changing to the proper directory prior to
               running MAILMGR.EXE.
               
               Mail Manager's operating environment should reflect what you've
               told Mail Manager to use.  If it doesn't, there's definitely a
               problem!
               
               DOS version must be 3.30 or above in order for Mail Manager
               +Plus+ to operate properly.
               
               DOS SHARE must be detected if you are operating in a NetBIOS
               environment.  The only exception is if you are running under a
               NOVELL network, in which case SHARE checking is bypassed.
               
               Flow control method can report one of five things:  Local mode,
               FOSSIL, RTS/CTS, XON/XOFF, or NONE.
               
               Free string space is pretty darned important, too.  This should
               really be up around 10,000 or higher at all times when you
               display this screen.  If it is less than that, we want to hear
               about it!
               
               Non-string array available is approximately the amount of free
               memory that is available for DSZ and your file
               compression/extraction programs.  If this number is less than
               200K, you are likely to run into trouble, and should check to
               make sure that you are EXITING, (NOT SHELLING!) from RBBS-PC to
               Mail Manager +Plus+.  The only other way that we can think of
               that would cause you to have less than 200K available on today's
               640K+ PC's would be if you have a VERY large # of conferences.
               If you have less than 200K here, you will probably need a
               utility like SHROOM (mentioned in the requirements section of
               this document) in order to use Mail Manager +Plus+.
               
               MAIN message base and user file names must match what is true
               for your MAIN area.  If not, you don't have MAIN as your 1st
               conference listed, and Mail Manager +Plus+ will NOT operate
               properly.
               
               Highest message number in MAIN, and highest message # that you
               read in main should be accurate.  If they're not, then Mail
               Manager +Plus+ didn't properly find you in the MAIN users file,
               and/or it wasn't able to correctly access the MAIN message file.
               
               Filename of list of protocol definitions should match what you
               told MAILCFG to use for MAILMGR.PRO.
               
               Filename of list of archivers should match what you told MAILCFG
               to use.  (If this file does not exist, Mail Manager will use the
               default type of compression that you chose, and will require
               said archiver to be in a DOS path!)


    MISCELLANEOUS CONSIDERATIONS                                    - Page 59 -


               
               Filename of FMS directory should match what is true for your
               system if you are using an RBBS-PC FMS directory, or "NONE"
               otherwise.
               
               The last four lines will only be shown to you if you are running
               under NetBIOS, and they are described in better detail elsewhere
               in this
               manual.
               
               If, after following these instructions, you continue to have
               trouble, take a look at the "COMMON PROBLEMS" section of this
               manual.


    MISCELLANEOUS CONSIDERATIONS                                    - Page 60 -


         HANDLING NON-STD PORTS VIA MAILMGR.PRO
         --------------------------------------
         
         The easiest way to handle nonstandard port addresses in Mail Manager
         +Plus+ is to create a separate configuration file for each node, and
         have each configuration file point to a different copy of MAILMGR.PRO.
         The downside of doing this is that every change you later make in your
         configuration will have to be duplicated for each node's configuration
         file.   It IS possible to achieve the same results with a single
         configuration file, however.
         
         In order to support a nonstandard port address in a single
         configuration file, have your MAILMGR.PRO specify a custom batch file,
         rather than a direct call to the protocol executable itself.  Your
         custom batch file can then send the correct commands to the protocol,
         depending on which port is involved.
         
         Here's what an entry in the MAILMGR.PRO file might look like.  (This
         should all be on one line, of course, but is split here for clarity):
         
                "Z)modem (Batch)",0,S,8,,B,1024,,0.95,,1=E,
                "X:\ZMODEM.BAT S [PORT#] [BAUD] [FILE]",
                "X:\ZMODEM.BAT R [PORT#] [BAUD] [FILE]"
         
         With drive X: of course being whatever drive\directory you want.
         
         Then the ZMODEM.BAT file could look something like (assuming that you
         have ports 1 and 2 at standard addresses, and port 3 at non-standard
         address 3e8, irq 5):
         
                   @ECHO OFF
                   : --------------------------------------
                   : 1st arg is either S or R,
                   : 2rd arg is comm port number
                   : 3rd arg is bps rate, and
                   : 4th arg is filename being transferred.
                   : --------------------------------------
                   IF (%1)==(S) GOTO SEND
                   IF (%1)==(R) GOTO RECEIVE
                   GOTO END
                   
                   :SEND
                     IF NOT (%2)==(3) dsz port %2 speed %3 sz -m %4
                     IF     (%2)==(3) dsz portx 3e8,5 speed %3 -m sz %4
                     GOTO END
                   
                   :RECEIVE
                     IF NOT (%2)==(3) dsz port %2 speed %3 rz %4
                     IF     (%2)==(3) dsz portx 3e8,5 speed %3 rz %4
                   
                   :END
         


    MISCELLANEOUS CONSIDERATIONS                                    - Page 61 -


         This could, of course, be refined into a single batch file that
         handles all protocols, not just Zmodem, but it should serve to
         illustrate the principle.  Or a separate batch file could be set up
         for each protocol.
         
         We leave it to you to adapt to protocol drivers other than DSZ.


    MISCELLANEOUS CONSIDERATIONS                                    - Page 62 -


         DESQVIEW, NETWORKS, AND MULTIPLE NODES
         --------------------------------------
         
         Operating in a multitasking environment or on a network is a special
         case, worthy of further explanation!
         
         First off, Mail Manager +Plus+ can automatically detect the following
         conditions:
         
               - Is DOS SHARE installed?
               - Is DESQview present?
               - Is Artisoft's LANtastic present?
               - Is Novell present?
         
         What Mail Manager +Plus+ detects will be used as the basis for
         initially determining the operating environment, which will be:
         
           - DESQview, if it is present, regardless of whether or not SHARE is
             installed.
           
           - NetBIOS, if DESQview is not present, and SHARE is installed, or
             Novell is detected.
           
           - Good ole' normal DOS if neither of the above is true.
         
         Mail Manager +Plus+ will then use the appropriate file locking
         technique for the type of environment that was detected.  At this
         point, the only file being accessed is Mail Manager's own
         configuration file, so your RBBS files are quite safe even if this is
         not the same environment that you have specified for RBBS to use.
         
         Once the program has progressed far enough to have read what network
         type that you told it to use (from DORINFOx.DEF if operating remotely,
         or MAILMGR.CFG if operating in local mode), Mail Manager +Plus+ will,
         if necessary, switch to your specified type of network.
         
         With that out of the way, let's talk about the three supported types
         of environments, and what they mean from the standpoint of Mail
         Manager +Plus+:
         
           DESQview - Mail Manager +Plus+ will use the same file & record
              locking scheme that RBBS-PC itself uses.  In fact, it uses the
              very same assembler source, which was written by Jon Martin in
              1988.  Therefore, the DESQview semaphore locking routines used by
              Mail Manager +Plus+ are copyrighted by Jon Martin, and are in
              fact available to anyone who has a copy of RBBS-PC's source code.
              Look for RBBSDV.ASM in RBBS-PC's assembler source.
           
           NetBIOS/ - This is a special case, and requires that physical file
              and Novell record locking take place.  RBBS-PC uses what is
              termed as a "semaphore" file, to control access to what Mail
              Manager +Plus+ is concerned with:  Your USERS file(s), your
              MESSAGES file(s), and your FMS file (if any).
              


    MISCELLANEOUS CONSIDERATIONS                                    - Page 63 -


              This is done with the hard-coded filename "IBMFLAGS", which will
              exist in the same directory as your MAIN message base.  If you're
              already running RBBS-PC under NetBIOS, look for it... it should
              already be there.  IBMFLAGS is 6 bytes in length, and contains
              nothing but three empty 2-byte records, which are controlled by
              RBBS-PC and Mail Manager +Plus+ to limit access to USERS and
              MESSAGES files.
              
              Under NetBIOS, Mail Manager +Plus+ will create and maintain its
              own "semaphore" locking file, using the same principle as
              IBMFLAGS.  The Mail Manager +Plus+ semaphore file is named
              MMFLAGS, and will be created in your Mail Manager +Plus+
              directory.  MMFLAGS will be 3 bytes in length, and manipulated by
              all nodes of Mail Manager +Plus+.
              
              It is also noteworthy to mention that all files will be opened in
              a SHARED fashion under NetBIOS, which is the nature of the beast.
              
              If you are running under Novell Netware, Mail Manager +Plus+ will
              detect it, and will not check for the installation of DOS SHARE.
              If Novell is not detected, yet NetBIOS is specified as the
              environment, Mail Manager will check for DOS SHARE before
              allowing itself to continue.
              
           DOS  - Gee, isn't it nice when you don't have to worry about all
              this?  Under good 'ole DOS, none of the above is meaningful, and
              all files will be opened normally, with no locking mechanisms in
              place.
         
         If you happen to be running in an environment that does NOT match any
         of the above three methods, AND you are sharing the same set of RBBS
         message bases and users files between nodes, you will want to consider
         having DOS SHARE loaded, and configure both RBBS-PC and Mail Manager
         +Plus+ to use NetBIOS as the operating environment.
         
         Or, if file sharing is not a concern, just configure Mail Manager
         +Plus+ to use DOS as its environment.
         
         For most installations, you can run up to 36 nodes from a single
         configuration file, utilizing a unique work directory for each node.
         Unusual installations (non-standard comm ports have already been
         discussed) can be accommodated via separate configuration files for
         one or more nodes.One such case might be a networked setup in which
         the network drive letters are not the same for each node (C:\MAINM.DEF
         on one, D:\MAINM.DEF on another).  Why you'd set your network up that
         way we don't know, but it isn't our place to, is it?


    MISCELLANEOUS CONSIDERATIONS                                    - Page 64 -


         WORKING WITH A FOSSIL DRIVER
         ----------------------------
         
         Mail Manager +Plus+ does support a FOSSIL driver.  If you told RBBS-PC
         to use a FOSSIL, Mail Manager +Plus+ will also.  The door has been
         tested extensively with both BNU v1.70 and X00 v1.2x FOSSILs.
         
         PLEASE NOTE that some door converters & programs that 'launch' doors
         for you may not correctly set the FOSSIL argument in DORINFOx.DEF!!!!
         
         The very last line of your DORINFOx.DEF (line #13) should be either a
         zero or minus one (0 or -1).  -1 indicates that the FOSSIL is active
         in RBBS-PC, and tells the door that it too should use a FOSSIL.
         
         To keep you from having to dig up the RBBS-PC documentation, here's
         what Mail Manager +Plus+ expects from DORINFOx.DEF:
         
         NEWARK CONNECTION  <- BBS name (ignored by Mail Manager +Plus+)
             CHIP               <- Sysop's first name
             MORROW             <- Sysop's last name
             COM1               <- Communications port
             2400 BAUDD,N,8,1   <- Communications parameters
              6                 <- Network type (4=DV, 6=NetBIOS)
             JOE                <- User's first name
             USERNAME           <- User's last name
             NEWARK, OH         <- User's city/state
             2                  <- User's graphics preference (2=ANSI)
             10                 <- User's security level
             30                 <- Number of minutes remaining
             -1                 <- FOSSIL in use (0=no, -1=yes)
             
             * NOTE - The second "D" in "BAUDD" is a bug in RBBS-PC 17.3C, and
             may or may not be present in your own DORINFOx.DEF files.
             Either way, it does not affect the operation of the door.
             
         It is possible to configure Mail Manager to ALWAYS check for a FOSSIL
         driver, regardless of the setting in DORINFOx.DEF.  This is done in
         the MAILCFG program, by setting the flow control method to "F".  In
         this case, Mail Manager +Plus+ will ALWAYS try to use a FOSSIL for
         communications.


    MISCELLANEOUS CONSIDERATIONS                                    - Page 65 -


         QWK NETWORKING
         --------------
         
         In addition to handling mail for individual callers, Mail Manager
         +Plus+ can also process QWK-formatted network mail packets for sharing
         conferences between bulletin boards.
         
         When used as the net host, Mail Manager +Plus+ can create the "net
         status" packets needed to interface with existing QWK-based network
         software such as TNET and RNET in use by node boards.
         
         For node operation, we provide a utility called MNET which converts a
         "net status" QWK packet from a host into a REP which can then be
         uploaded into the node BBS's QWK door.  MNET also does the reverse
         conversion, taking messages exported from the node system via a QWK
         and converting them to a REP that can then be uploaded to the host
         system.  This eliminates the need for a separate network interface
         such as RNET.  Although MNET is ideal for use with a Mail Manager
         +Plus+ system (and MMGR+ has several enhancements that allow them to
         work well together) MNET may be used with any system capable of
         exporting QWK packets and receiving REP packets.
         
         Since this subject is a fairly complex one, details are handled in a
         separate file called NETINFO.DOC.
         
         
         COMPRESSING THE EXECUTABLE FILES
         --------------------------------
         We're distributing the executables in non-compressed format.  You'll
         find that our .EXE's will compress quite nicely with utilities like
         PKLITE and LZEXE.  We leave it up to you to use the compression
         utility of your choice, or run as-is.
         


    MISCELLANEOUS CONSIDERATIONS                                    - Page 66 -


         SECURITY FEATURES
         -----------------
         
         Mail Manager +Plus+ has extensive built-in security functions.  We
         hope you agree that it does make for a pretty secure mail door.
         
         We want to make you aware of the importance of the security level that
         you configured in the MAILCFG program for the ability to read ALL
         messages.  This security level is checked for all of the SysOp
         functions that Mail Manager +Plus+ performs, and should be set to
         either SysOp or Co-SysOp level only!  Some of the more important
         things that users with this security level or higher can do:
         
         - Use the SysOp-only function I)nfo from the main menu (which shows
           where everything that pertains to your Mail Manager +Plus+ setup is
           located).
           
         - Upload a message under a name other than the one that they use on
           the BBS, regardless of the setting of the "Alias file" argument in
           the MAILCFG program for that conference.
           
         - Read everybody's mail, regardless of whether it's marked as private
           or password-protected.
           
         - Use the C)rash option when uploading netmail messages, and also the
           file attach and request options.
           
         You get the idea.
         
         Contrary to some of the concerns we have received on this subject over
         the last few years, a user CANNOT inadvertently download a mail packet
         that was extracted by a previous user of the door.  Mail Manager
         +Plus+ temporarily keeps the mail packet on disk so that the SysOp can
         check it out for appearance, if there were any problems in the
         transfer, etc.  Mail Manager +Plus+ deletes any existing mail packet
         whenever a user attempts to D)ownload, E)xpedite, or U)pload.
         
         Conferences are configured with two minimum security levels:  One for
         the ability to read, and the other for the ability to post.
         
         Users can only extract mail from conferences that they have joined
         (either from the BBS itself, or via Mail Manager +Plus+, if you have
         turned "on" this ability in the MAILCFG program).
         
         Mail Manager +Plus+ will add a user to a conference only if you have
         specified that it is OK to do so in the MAILCFG program.
         
         Mail Manager +Plus+ bypasses all killed messages.
         
         Password-protected messages are only extracted and downloaded to users
         with an exact name match in the "TO" or "FROM" fields, or to those
         with sufficient security to read ALL messages.
         


    MISCELLANEOUS CONSIDERATIONS                                    - Page 67 -


         With two exceptions, only users with sufficient security to read ALL
         messages are permitted to upload messages under a name other than the
         one they use on the BBS.  The exceptions are:
         
         - If you have configured Mail Manager +Plus+ to look for an ALIAS file
           for a given conference, it will accept messages from the user's pre-
           defined alias, and will change the user's real name to his alias
           before posting.
           
         - If you have configured a specific username for "net status" QWK
           network capability, that username will be able to upload messages
           with any name in the "FROM" field.
           
         
         Users cannot upload messages to conferences that they have not joined.
         
         Mail Manager +Plus+ posts a private message (in the MAIN area) to the
         sender's true name whenever a security violation regarding an uploaded
         reply occurs.  This can be triggered by:
         
         - Uploading a message with the "FROM" name not matching the user's
           name on the BBS or his pre-defined alias.
           
         - Uploading a message to a conference that the user has not joined.
           
         - Uploading a message to a conference that the user does not have
           sufficient security to post a message in.
           
         - Uploading a message to a conference number that does not exist.
           
         Files listed in your FMS directory that were uploaded as "SYSOP-ONLY"
         will be listed only in the SysOp's own mail packets.  They will be
         bypassed for everyone else.


    MISCELLANEOUS CONSIDERATIONS                                    - Page 68 -


         ADDITIONAL FEATURES
         -------------------
         
         CHAT MODE:  While Mail Manager +Plus+ is waiting for a keystroke
                     (preferably at the MAIN MENU), the Sysop can press [F10]
                     to jump into a no-frills chat mode with the user that's
                     currently online.
                     
                     When finished with the chat, either one of you can type
                     "/QUIT" to return to Mail Manager.
         ----------------------------------------------------------------------
         DOS SHELL:  While Mail Manager +Plus+ is waiting for a keystroke
                     (again, preferably at the MAIN MENU), the Sysop can press
                     [F2] to jump to DOS.  When finished, type EXIT to return
                     to Mail Manager +Plus+.  Naturally, this works only from
                     the local keyboard.  Mail Manager +Plus+ will
                     automatically return to the proper drive and directory, no
                     matter where you are when you type "exit" to return from
                     the DOS shell.
         ----------------------------------------------------------------------
         TIME LIMIT: This is passed to Mail Manager +Plus+ from RBBS-PC in
                     DORINFOx.DEF.  It will be either the amount of time
                     remaining on your RBBS-PC, or whatever time limit that you
                     specified in DOORS.DEF, otherwise.  In local mode, the
                     time limit is always 120 minutes.
         ----------------------------------------------------------------------
         KYBD IDLE:  If Mail Manager +Plus+ has to wait more than 180 seconds
                     for the user to press a key, it will exit back to the BBS.
                     The user will get a beep and a warning message after 90
                     seconds, and every 30 seconds thereafter, until keyboard
                     time expires.
         ----------------------------------------------------------------------
         CARRIER DETECT:  If the user drops carrier, Mail Manager +Plus+ will
                     report to you as such, write this info to the appropriate
                     log file, and return to the BBS.  RBBS-PC will see that no
                     carrier detect is present, re-cycle itself, and wait for
                     the next caller.
         ----------------------------------------------------------------------
         DOWNLOAD & EXIT:  Although the E)xpedite! option is documented
                     elsewhere in this manual, we didn't make it clear as to
                     the best way to automate this from RBBS-PC's standpoint.
                     
                     RBBS-PC 17.3C and above allow you to specify "/G" after
                     the name of the door, which allows the user to be logged
                     off immediately after returning to RBBS-PC.  Therefore,
                     the user could type:  "d mailmgr /g".
                     
                     Then, from within Mail Manager +Plus+, select E)xpedite!,
                     and the user will be logged completely off the BBS after
                     downloading their mail.
                     
                     As an alternative, you can choose to have the door drop
                     DTR whenever G)oodbye and E)xpedite! are chosen.  Please
                     read the warning message about this option elsewhere in
                     this documentation!


    MISCELLANEOUS CONSIDERATIONS                                    - Page 69 -


         ----------------------------------------------------------------------
         NEW FILES:  If you are running a standard RBBS-PC FMS directory, you
                     should be able to use this built-in capability.  If you
                     are not running a standard FMS, and the path/name of your
                     FMS directory is set to "NONE" in the MAILCFG program,
                     Mail Manager +Plus+ will not attempt to include a new file
                     listing in the user's mail packets.
                     
                     It should be noted here that the users do have the ability
                     to turn this feature "off", if they do not desire a file
                     listing in their mail packets.
                     
                     Here's what is required of your FMS directory:
                     
                     - No 'special' lines contained within it (semi-private
                     filenames preceded with an asterisk (*) before the
                     filename, special comment lines, etc).
                     
                     - Oldest files listed at the top of the FMS, and most
                     recent files listed at the bottom.
                     
                     If yours fits all of the above, NEWFILES should work fine.
                     
                     Here's the way NEWFILES works:
                     
                     1) Finds the date that the user last checked the file
                        listing (from the RBBS-PC main users file).  If user
                        never listed your file directories, the user's last
                        date into the Mail Manager +Plus+ door is used,
                        instead.
                        
                     2) Grabs the very first line of your FMS, to determine the
                        line length, since this can vary depending on how you
                        set
                        things up via RBBS-PC's CONFIG.  HOWEVER, all lines in
                        your FMS are expected to be the same length as the
                        first line listed!
                        
                     3) After determining line length, moves to end of file,
                        grabs the very last line of your FMS, and checks the
                        date stamp against the user's "last check" date.
                        
                     4) If the last file's date is the same as, or newer than,
                        the user's date that they last listed your files,
                        NEWFILES steps through your FMS in reverse order,
                        pulling out filenames & extended descriptions until the
                        date stamp is earlier than the user's last check.  The
                        file created (NEWFILES.DAT) is then included in the
                        user's QWK mail packet, and can be viewed easily within
                        his mail reader.
                        
                        If the last file's date is older than the user's last
                        check, NEWFILES figures no new files, and doesn't
                        include a NEWFILES.DAT in the QWK packet.
                        


    MISCELLANEOUS CONSIDERATIONS                                    - Page 70 -


                     PRIVATE UPLOADS TO THE SYSOP are listed ONLY in the
                     sysop's own mail packets.  These files (and their extended
                     descriptions) are skipped for everyone else.
                     
                     If you use chained FMS directories, or any of the "\FMS"
                     directives, NEWFILES will stop searching when it reaches
                     that line of your FMS.  Why?  The line won't be an
                     extended description  ("  ." as the last three characters
                     on the line), and won't have a file date in the proper
                     positions on the line.  In this case, NEWFILES will
                     consider the file date to be 00-00-00, and will quit
                     searching your FMS directory.
                     


     UTILITY PROGRAMS BUNDLED WITH MAIL MANAGER +PLUS+              - Page 71 -


         We supply several utility programs to aid in your setup and operation
         of Mail Manager +Plus+.  A quick overview:
         
         
         MailCFG, the configuration program:
         
            We recommend using MailCFG to configure Mail Manager +Plus+.
            MailCFG directly edits the binary configuration file, and is easy
            to use.  MailCFG is covered in the separate section of this manual
            entitled:  "CONFIGURING MAIL MANAGER +PLUS+".
            
         CFG2TXT & TXT2CFG - the binary<-->text utilities:
         
            Throughout Mail Manager's relatively short life, we have heard from
            several SysOps who simply do not care for the configuration program
            MailCFG.  These two utilities are provided as an alternative, and
            also to ease the installation of FIDO *.MSG message areas.
            
         MailFix, the *M.DEF purge/repair utility:
         
            A handy utility intended as an alternative (or replacement) for
            RBBS CONFIG's "repair" facility, MU-EDIT, and similar utilities.
            MailFix has the ability to keep a physical number of messages in a
            given message base (handy for echo areas), purge killed messages,
            and repair damaged messages.  MailFix can also renumber message
            bases and reset user message pointers according to the new message
            numbers.
            
         MMIndex, the indexing program for *.MSG areas:
         
            Optional (but HIGHLY RECOMMENDED!) utility for SysOps running Fido
            *.MSG message areas.  This program has no meaning if you are
            running only RBBS-PC *M.DEF message bases.
            
         MMGRNode, the nodelist compiler:
         
            Optional (but HIGHLY RECOMMENDED!) utility to compile raw nodelists
            into a shortened binary format readable by Mail Manager +Plus+.
            Useful only if you are running an *.MSG netmail area or two.
            
         MNET, the QWK network conversion utility:
         
            This utility is used only on the "node" end of a QWK network, and
            can be used with ANY BBS type that has a QWK mail door capable of
            handling MarkMail-compatible network mail packets.
            
         MUSER, the Mail Manager +Plus+ user file editor:
         
            A utility to edit/purge/manipulate Mail Manager's internal users
            file, MAILMGR.USR.  This utility was created to handle QWK network
            usernames, but has other obvious uses as well.
            
         The following pages describe these programs in greater detail.


     UTILITY PROGRAMS BUNDLED WITH MAIL MANAGER +PLUS+              - Page 72 -


         CFG2TXT & TXT2CFG
         -----------------
         
         Mail Manager +Plus+ uses a binary configuration file, which can be
         directly edited by the configuration program, MAILCFG.EXE.  However,
         there are some situations where MAILCFG becomes repetitive, and there
         are many SysOps who have expressed the desire for a text
         configuration.
         
         So... to address the above, these two utilities are provided.
         
         The two programs are companions:  CFG2TXT converts a binary
         configuration file into text format, and TXT2CFG converts a text file
         to Mail Manager +Plus+ binary configuration format.
         
         Usage of these programs:
         
           CFG2TXT [INPUT.FIL] [OUTPUT.FIL]
         
               Where INPUT.FIL is the name of the Mail Manager +Plus+ binary
               configuration file to convert, and
               
               OUTPUT.FIL is the name of the text file to create.
               
               If nothing is passed on the command line, CFG2TXT will default
               to:
               
                          INPUT.FIL  = MAILMGR.CFG
                          OUTPUT.FIL = MAILMGR.TXT
               
           TXT2CFG [INPUT.FIL] [OUTPUT.FIL]
         
               The reverse of the above.  INPUT.FIL is the name of the text
               file to convert, and OUTPUT.FIL is the name of the binary
               configuration file to create.  If nothing is passed on the
               command line, TXT2CFG will default to:
               
                          INPUT.FIL  = MAILMGR.TXT
                          OUTPUT.FIL = MAILMGR.CFG
               
               Each line in the text configuration file must be flush left.
               The supplied MAILMGR.TXT file should be pretty self-explanatory,
               but here is the run-down:
               
               Lines beginning with a semi-colon ";" are ignored as comments.
               ANY BLANK LINES WILL BE CONSIDERED PART OF THE CONFIGURATION!
               Lines without semicolons (the order in which TXT2CFG will read
               them) are as follows:


     UTILITY PROGRAMS BUNDLED WITH MAIL MANAGER +PLUS+              - Page 73 -


                        MAX = Maximum number of characters,
                        INT = Integer (cannot exceed 32767)
                        
               Line #  Meaning                                           MAX
               ------  ------------------------------------------------  ---
                1      Name of your RBBS-PC.                              35
                2      Name you use to log onto your BBS remotely.        31
                3      Your first name as you are known to your users.    15
                4      Your last name as you are known to your users.     15
                5      Security level to read *ALL* messages everywhere  INT
                6      Security level to use when operating locally.     INT
                7      Graphics to use locally (0=no, 1=ascii, 2=ansi)     1
                8      Default tagline to use for ALL conferences.        61
                9      First eight characters for packet filenames.        8
               10      Default file compression (ARC,ARJ,LZH,ZIP only)     3
               11      Path/Name of news file - *NON-GRAPHIC* version.    40
               12      Path/Name of list of system bulletins.             40
               13      Type of network to use in local mode. (D,N,Q)       1
               14      Type of handshaking to use remotely (F,R,X,N)       1
               15      Path/filename of your FMS directory (optional)     40
               16      Path/filename of your list of available archivers  40
               17      Environment variable pointing to XFER-x.DEF        15
               18      Modify REP time stamp to system date/time? (Y,N)    1
               19      City/State where your BBS is located.              31
               20      Your BBS phone number.                             12
               21      Character to use for smart text (default=123)       3
               22      Default path to *M.DEF conferences.                40
               23      Path/filename of echo toss log.                    40
               24      Start of timelock.  Use 24-hour clock (HH:MM)       5
               25      End of timelock.    Use 24-hour clock (HH:MM)       5
               26      Allow door to drop DTR at G)oodbye, E)xpedite!      1
               28      Show empty/unjoinable conference?                   1
               
               28 and up = Conference configuration section.  Each conference
               is configured as follows (22 arguments = 21 commas on each
               line):
               
               1,2,"3","4",5,6,7,8,"9",10,11,12,"13",14,15,16,17,18,19,20,21,
               "22"  (all on one line).
               
                            MAX = Maximum number of characters,
                            INT = Integer (cannot exceed 32767)
               
               Arg #      Meaning                                           MAX
               ------     ------------------------------------------------  ---
                  1       Conference number (1 to 500).                       3
                  2       Conference name                                     7
                  3       Path/Name of this conference's USERS file.         80
                  4       Path/Name of this conference's MESSAGES file.      80
                  5       Allow or dis-allow ANSI (Y or N).                   1
                  6       Allow or dis-allow high/low ASCII (Y or N).         1
                  7       Security level needed to read this conference.    INT
                  8       Security level needed to post in this conference. INT
                  9       Tagline for this conf (NONE = use default tag).    61
                 10       Modify mail reader tearlines? (Y or N).             1


     UTILITY PROGRAMS BUNDLED WITH MAIL MANAGER +PLUS+              - Page 74 -


                 11       Type of msg base (Y=fixed, N=elastic, F=FIDO).      1
                 12       Allow users to join from within the door? (Y, N).   1
                 13       Path/Name to alias file (leave empty if none).     80
                 14       Zone for this conf (applies to FIDO areas only)   INT
                 15       Net  for this conf (applies to FIDO areas only)   INT
                 16       Node for this conf (applies to FIDO areas only)   INT
                 17       Is this a FIDO *.MSG NETMAIL area? (Y or N).        1
                 18       Add tear/origin line (Y or N)  (FIDO areas only)    1
                 19       True FIDO symbolic area name (FIDO areas only)     15
                 20       Allow private messages in this conference? (Y/N)    1
                 21       Max # of lines per msg for this conference (1-99)   2
                 22       Conference description.                            25
               
               Your MAIN RBBS-PC MESSAGE BASE must be listed as conference #1!
               From there on, you can mix/match as you see fit.  Your MAIN
               conference might look something like this:
               
               
               1,MAIN,"C:\RBBS\MAINU.DEF","C:\RBBS\MAINM.DEF",Y,Y,5,5,"NONE",N,
               N,N,"NONE",0,0,0,N,N,"",Y,99,"Main message base"
               
               NOTE that it should all be on one line!  It is split here for
               the purposes of this documentation.  This line tells Mail
               Manager that:
               
               This is conference #1, named "MAIN".
               The path to the users file is "C:\RBBS\MAINU.DEF".
               The path to the messages file is "C:\RBBS\MAINM.DEF".
               Both ANSI and high/low ASCII are allowed in uploaded replies.
               Users with security level 5 and above can both read and reply.
               Default tagline will be used.
               We are not bothering with FIDO-STYLE tearlines.
               This is an "elastic" message base.
               Users cannot join this conference from within the door.
               There is no alias file for this conference.
               This is not an *.MSG Fido-style area.
               Private messages will be allowed.
               99 maximum lines per message.
               Conference description is "Main message base".
               
               ----------------------------------------------------------------
               
               ...and that's the way it works.  Conferences do NOT have to be
               listed in numerical order: MAILCFG will handle them no matter
               where they are in the list.  HOWEVER, if you need "gaps" between
               conference numbers, pay close attention to the following:
               


     UTILITY PROGRAMS BUNDLED WITH MAIL MANAGER +PLUS+              - Page 75 -


               *PLEASE NOTE* - TXT2CFG will *NOT* automatically "fill-in-the-
               blanks" for you.  This INCLUDES conference numbers!  If you
               intend to reserve a space for a conference, set the conference
               name to "{EMPTY}".  The bare minimum line to reserve a
               conference would look like this:
               
               X,{EMPTY},,,,,,,,,,,,,,,,,,,,
                 
                 (Yes, that's 21 commas).  Replace "X" with the conference
                 number.
                 
               If you intend to leave gaps in conference numbers, you will have
               to add one of these lines for every conference in question.
               TXT2CFG will completely ignore any unused conference numbers,
               meaning that if your text configuration looks like this:
               
                   1,MAIN,.....
                   3,CONF3,.....
               
               TXT2CFG will convert them to:
               
                   1,MAIN,.....
                   2,CONF3,.....
               
               But, if you configure it like this:
               
                   1,MAIN,.....
                   2,{EMPTY},.....
                   3,CONF3,.....
               
               TXT2CFG will import them that way, and "reserve" conference #2.


     UTILITY PROGRAMS BUNDLED WITH MAIL MANAGER +PLUS+              - Page 76 -


         MAILFIX
         -------
         
         MailFIX is an alternate purge/repair utility for RBBS-PC message
         bases.  Because of its obvious utility for all RBBS sysops, we are
         releasing it as a separate stand-alone utility as well.
         
         Version 4 is much faster than previous releases, and has a few more
         useful options than previous versions.
         
         USAGE:
         
           MAILFIX [options] D:\PATH\MESSAGE.FIL
         
           Available options:
         
            /V - Only View the integrity of the message file.  Do not perform
                   the actual repair work, and do not create an output file.
                   
            /D - Use DOS screen writes instead of direct.  Slows the program
                   down a tad, but allows for DOS redirection of output.
                   
            /F - Informs MAILFIX that this is a fixed-length message base.  If
                   "/F" is not chosen, MAILFIX assumes the message base to be
                   configured as 'elastic'.
                   
            /R - Informs MAILFIX that the sysop uses RBBSMail or MsgToss on
                   this message base.  Both of these mail processors format the
                   time field in the message header with a period instead of a
                   colon, which CONFIG's option #185 (repair messages) chokes
                   on.
            
            /O - Informs MAILFIX that the sysop uses OverMail on this message
                   base.  OverMail formats the time field in the message header
                   with a semicolon instead of a colon, which CONFIG's option
                   #185 (repair messages) chokes on.
                   
            /Knnn - (Where "nnn" is the number of messages to keep.): Tells
                   MAILFIX to trim down the physical size of the message base,
                   regardless of whether or not the messages to delete are
                   flagged as "killed".  This is useful for things like an echo
                   area that grows almost out of control daily. If you want to
                   keep 50 messages, your switch would be "/K50".
                   
                   This switch may not be used in conjunction with "/V"!
                   
                   Use of this option will OVERWRITE your original message
                   file!
                   
            /N - Tells MAILFIX to renumber the message base, starting at
                   message number 1.  If used with the /K option, the retained
                   messages will be renumbered starting with 1.
                   
                   Use of this option will OVERWRITE your original message
                   file!


     UTILITY PROGRAMS BUNDLED WITH MAIL MANAGER +PLUS+              - Page 77 -


                   
                   Optionally, you may immediately follow the /N with the
                   drive:\path\filename of the user file for this message base
                   if you wish MAILFIX to update the user's message pointers to
                   reflect the renumbering.  There can be no spaces between the
                   /N and the beginning of the filename.  Your original user
                   file will be updated in place, so if you want a backup of
                   your unaltered user file, you must make one first.
                   
                   D:\PATH\MESSAGE.FIL is the name of the messages file to
                   purge/repair.
                   
         Unless the /V option is used, MAILFIX will create an output file with
         the same name and the extension '.FIX'.  Above example would create
         D:\PATH\MESSAGE.FIX.
         
         If the /Knnn or /N switches are used, MAILFIX will make a second
         pass on your message base, using the *.FIX file for input, and the
         original file name for output.  When finished your original message
         file will have been replaced by MAILFIX's work, and the *.FIX file
         will be deleted.
         
         EXAMPLES:
         
         Unless you use the "/Knnn" or "/N" command line options, MAILFIX will
         not overwrite (or modify in any way) your original message file.  If
         you want to replace your old message file with the one that MAILFIX
         creates, your best bet is to run MAILFIX from a batch file, like so:
         
            MAILFIX C:\RBBS\MAINM.DEF
            IF EXIST C:\RBBS\MAINM.FIX DEL C:\RBBS\MAINM.DEF
            IF EXIST C:\RBBS\MAINM.FIX REN C:\RBBS\MAINM.FIX C:\RBBS\MAINM.DEF
            
         On the other hand, if you have an echo area that's scanned by
         RBBSMail, and you want to keep it purged down to 100 messages, your
         command line would be:
         
            MAILFIX /R /K100 C:\RBBS\FILENAME.DEF
         
         If you want to also renumber the message base, and to update the
         pointers in your user file for this base:
         
            MAILFIX /R /K100 /NC:\RBBS\USERFILE.DEF C:\RBBS\FILENAME.DEF
         
         If you wanted to do the same thing with a message base that's been
         scanned by OverMail:
         
            MAILFIX /O /K100 /NC:\RBBS\USERFILE.DEF C:\RBBS\FILENAME.DEF
         
         These last three examples would replace "FILENAME.DEF" with the
         fixed/purged/pruned message base.
         
         Run MAILFIX without a command line to get a help screen.
         
         


     UTILITY PROGRAMS BUNDLED WITH MAIL MANAGER +PLUS+              - Page 78 -


         TECHIE STUFF ABOUT MAILFIX FOR THOSE WHO CARE:
         ----------------------------------------------
         
           If you run a mail system that utilizes RBBSMail, MsgToss, or
           OverMail for echo mail processing, you're likely to have run across
           the fact that the repair utility out of CONFIG (option #185) no
           longer works for you.  This is due to the fact that these mail
           processors place either a period or a semicolon in the time field of
           the message header on every message that they process.
           
           This just happens to be one of CONFIG's five "key fields" that it
           looks at to determine whether or not the message is corrupt.
           
           These key fields are:
           
           Description                                  Should be
           -------------------------------------------  ---------
           The "killed" flag,                           Ascii 225 or 226 "á,â"
           the first separator in the 'time' field,     ":"
           the second separator in the 'time' field,    ":", ".", or ";"
           the first separator in the 'date' field,     "-"
           and the last separator in the 'date' field.  "-"
           
           Therefore, this string of five characters is very important, and is
           what will be displayed to you if the message needs repaired, and you
           specify the "/v" option on MAILFIX's command line.  If you don't
           specify "/v" on the command line, MAILFIX will do its best to fix
           the message, and report "<fixed>".
           
           If you use a mail processor on your RBBS-PC message bases OTHER than
           RBBSMail, MsgToss, or OverMail, and said mail processor *DOESN'T*
           use a period or semicolon as its 'mark' in the second separator in
           the TIME field, we'd sure like to hear about it so that we can
           attempt to make MailFix compatible with your system.
           
           WHEN, AND HOW MAILFIX FIXES A MESSAGE:
           -------------------------------------
           
           To determine whether or not a message is valid, MAILFIX looks at the
           following in the message header:
           
                Message number             - Should never be zero.
                Killed flag                - Should always be ASCII 225 or 226.
                Number of 128-byte records - Should never be less than 1.
           
           If the message header passes these three tests, MAILFIX assumes it
           has a valid message on its hands, and moves on to do one of three
           things:
           
           - Copy it (if it isn't marked as killed, and doesn't need fixed).
             
             MAILFIX will step through the message's records and write them to
             the output file.
             


     UTILITY PROGRAMS BUNDLED WITH MAIL MANAGER +PLUS+              - Page 79 -


             - Fix it (if it isn't marked as killed).
             
             If, during all of its checks, MAILFIX finds that it has a valid
             message on its hands, yet the five key characters mentioned above
             DON'T MATCH what they're supposed to, the message header is
             adjusted as follows:
             
               * Sets the "killed" flag to indicate that this is an active
                 message (Ascii 225) "á".
               
               * Sets the TIME separators to:
                   :: - RBBS-PC  (un-scanned by RBBSMail/OverMail)
                   :. - RBBSMail and MsgToss
                   :; - OverMail
               
               You must have specified "/R" or "/O" on the command line for the
               RBBSMail/OverMail checks to take place.
               
               If "/R" or "/O" is specified, MAILFIX is smart enough to
               discover whether or not the message has been scanned by either
               one of these mail processors yet, and will not mark an un-
               scanned message with the special "." or ";" separator.
               
               * Sets both DATE separators to "-".
               
             - Purge it (if it's marked as killed).
             
             MAILFIX will skip the entire message (and its records) if the
             message is marked as killed (ASCII 226) "â".
             
         If the message didn't pass the tests, MAILFIX assumes that this is not
         a message header, reports to you as such, purges the offending record,
         and moves on to the next one.
         
         
         
            *=- ABOUT MAILFIX and MESSAGE BASES with CARBON COPIES -=*
                --------------------------------------------------
         
         MailFix *DOES* work with message bases that have been configured with
         the "carbon copy" feature of RBBS-PC v17.4+.  MailFix does not go
         through any special gyrations to look for multiple-recipient messages,
         but it will not trash your message base, either.  When renumbering, it
         will reset the message number in all "carbon copies".
         
         In the nearly 2 years of Mail Manager / Mailfix's life thus far, we
         have found that there are MANY utilities floating around out there
         that do not strictly adhere to the RBBS-PC message format as-defined
         in the documentation for our favorite BBS software.  MailFix was
         specifically written to be as generic as possible, and to work with
         the widest possible variety of RBBS-PC message bases.
         


     UTILITY PROGRAMS BUNDLED WITH MAIL MANAGER +PLUS+              - Page 80 -


         The only incompatibility with RBBS-PC v17.4 message bases is the
         following scenario:
         
         The message base is configured with "carbon-copy" turned on, and
         
         1) - The very first header of the "carbon-copy" message is bad, or
                 2) - The very first header of the "carbon-copy" message is
                 marked as "killed".
                 
         In the first case, MailFix will skip the "bad" message, and maybe the
         one following it as well, until it can get its bearings and find the
         next "good" message header.
         
         In the second case, Mailfix will purge the entire message, even if
         some of the other carbon copies have not been marked as killed.


     UTILITY PROGRAMS BUNDLED WITH MAIL MANAGER +PLUS+              - Page 81 -


         MMINDEX
         -------
         
         MMIndex is the Mail Manager Plus indexing utility for Fido-style *.MSG
         message areas.  If you are not running any of these types of message
         areas, you do not need MMIndex, and can skip this section.
         
         Usage:  MMINDEX [X:\PATH\MAILMGR.CFG] [/Confnum]
         
         If nothing is supplied on the command line, MMIndex will look for a
         file named MAILMGR.CFG in the current directory, and process all Fido
         conferences.
         
         If "/confnum" is supplied on the command line, MMIndex will process
         ONLY that individual conference number.  You can only supply one
         individual conference on the command line.  For example:
         
           MMINDEX E:\MMGR\MAILMGR.CFG /4
         
         ..would process conference #4 only, using the E:\MMGR\MAILMGR.CFG
         configuration file.  If "/confnum" is omitted, MMIndex will process
         all Fido conferences listed in the configuration file.
         
         MMIndex reads the Mail Manager +Plus+ binary configuration file, and
         looks for all conferences configured as F)ido (*.MSG).  It then
         creates a file named MMGR.NDX in each FIDO *.MSG subdirectory, which
         is what Mail Manager +Plus+ uses to move as quickly as possible
         through the messages within.  The index is 4 bytes per message, so if
         you have 100 messages in a FIDO conference, MMGR.NDX should be 400
         bytes in length.
         
         Mail Manager +Plus+ creates/updates the index file, but you will save
         yourself (and your users) some time by putting MMINDEX.EXE in your
         nightly event.  If you renumber your messages in the middle of the
         night, Mail Manager +Plus+ will find that the index in each conference
         is invalid, and will have to re-create it from scratch.  MMINDEX
         deletes any pre-existing indexes, and creates new ones in their place.
         
         If you are running FIDO *.MSG conferences, you should put MMINDEX in
         your nightly event (after your renumbering/maintenance) as the very
         LAST thing before your BBS comes back up.


     UTILITY PROGRAMS BUNDLED WITH MAIL MANAGER +PLUS+              - Page 82 -


         MMGRNODE
         --------
         
         MMGRNODE.EXE is meaningful only if you are running one or more FIDO
         *.MSG netmail areas.  If you are not configuring any such areas into
         Mail Manager +Plus+, you have no need for this utility.
         
         Mail Manager +Plus+ uses a proprietary compiled nodelist format for
         all Zone:Net/Node searches in your netmail areas.  Although it is not
         absolutely necessary to use our implementation, you will lose the
         convenience of being able to confirm that you are sending netmail to
         the correct Zone:Net/Node, and will have to blindly enter in your
         Zone:Net/Node arguments for netmail messages that you upload into Mail
         Manager +Plus+.
         
         MMGRNODE reads a "raw" nodelist, and compiles it into a format that is
         optimized for small file size and fast searches.  MMGRNode can use a
         single nodelist, or can combine several different ones together.
         
         Usage:  MMGRNODE [/A] X:\PATH\NODELIST.FIL
         
               /A = Instructs MMGRNODE to append to any pre-existing compiled
               nodelist that it created previously.  If no "/A" on command
               line, MMGRNODE will create the compiled nodelist and index from
               scratch, overwriting any pre-existing ones.
               
               X:\PATH\NODELIST.FIL = The path/filename of the raw nodelist
               that you wish to compile.
               
               MMGRNODE should always be run from your Mail Manager +Plus+
         directory.  It creates the following two files whenever it is run:
         
         MMGRNODE.DAT  - The main data file containing Zone, Net, and node
         numbers, as well as SysOp name, and BBS phone number.
         
         MMGRNODE.DIX  - The main data file's index (MUCH smaller in size).
         
         If you intend to compile several different nodelists together, it is
         important to consider which list contains the addresses that you will
         want to access frequently, and also the physical size of the nodelist
         itself.  For instance, if you ever need to send something to someone
         in RBBS-NET, and you intend to compile both the RBBS-NET and FIDO-NET
         nodelists, you may want to compile the RBBS-NET list first, since the
         file size is so small.  The search time to get through RBBSLIST is
         minimal in comparison to having to scan the entire FIDO nodelist just
         to find someone in RBBS-NET.  To compile using this scenario, your
         command lines would be:
         
            MMGRNODE X:\PATH\RBBSLIST.178
            MMGRNODE /A X:\PATH\NODELIST.094
         
         This would create the two files MMGRNODE.DAT and MMGRNODE.DIX from
         scratch, starting with the RBBS-NET nodelist.  The FIDO-NET nodelist
         would then be appended to them.


     UTILITY PROGRAMS BUNDLED WITH MAIL MANAGER +PLUS+              - Page 83 -


         MNET
         ----
         
         MNET.EXE is the QWK->REP file conversion utility for QWK networks.
         This program is available separately, and can be used with BBS types
         other than RBBS-PC.
         
         Usage:  MNET HOSTNAME [I] [O]
         
         HOSTNAME = The name of the configuration file that MNET is to use for
               this session (HOSTNAME.CFG).  HOSTNAME.CFG will then be read for
               operating parameters, and the program will look for HOSTNAME.QWK
               in the directory you specify.
               
               I = Import mode; convert existing HOSTNAME.QWK to BBSNAME.REP,
               for later processing by Mail Manager +Plus+ itself.
               
               O = Export mode; convert existing BBSNAME.QWK to HOSTNAME.REP,
               for later uploading to the host system.
               
               You can have as many configuration files as necessary for your
         installation.  The format of each configuration file is like so:
         
             <<START OF EXAMPLE>>
         
         NODE                                           ; NODE PACKET NAME
         NODESYSOPFIRST NODESYSOPLAST                   ; NODE SYSOP NAME
         HOSTSYSOPFIRST HOSTSYSOPLAST                   ; HOST SYSOP NAME
         C:\MAILMGR\NODE5\                              ; NODE PACKET DIRECTORY
         C:\MAILMGR\NODE5\                              ; HOST PACKET DIRECTORY
         My own personal BBS (123) 456-7890             ; NODE TAGLINE
         The remote system I am calling (123) 456-7890  ; HOST TAGLINE
         PKZIP -es [FILE]                               ; PACK COMMAND LINE
         PKUNZIP -o [FILE]                              ; UNPACK COMMAND LINE
         
         ; ALL REMAINING LINES CONSIST OF THREE PARAMETERS, SEPARATED BY COMMAS
         ; NODE CONF, HOST CONF, PRIVATE ALLOWED (Yes, No, Convert priv to pub)
         
         19, 4, Y
         
             <<END OF EXAMPLE>>
         
         MNET converts the word "SYSOP" to the true sysop name in question, as
         listed in the HOSTNAME.CFG file, whenever it is found in the TO or
         FROM names, appropriately.
         
         The supplied NETINFO.DOC explains the use of this program in greater
         detail.


     UTILITY PROGRAMS BUNDLED WITH MAIL MANAGER +PLUS+              - Page 84 -


         MUSER
         -----
         
         MUSER.EXE is the Mail Manager +Plus+ editor for the door's internal
         users file, MAILMGR.USR.
         
         The program was created for the purpose of setting up "net status
         usernames" for the HOST sysop in QWK networks, but quickly evolved
         into a useful utility for general aspects of Mail Manager +Plus+
         maintenance.
         
         It can, for example, be run periodically to purge users from the
         internal MAILMGR.USR file that have not opened the door in xx number
         of days.  This can speed up operation, since the door will not have to
         scan through as many records in the file in order to find everyone
         when they load the door.
         
         The utility is meant to be run from within your Mail Manager +Plus+
         directory, and will look for MAILMGR.USR when it loads.  Optionally,
         you can specify the path/name of the users file on the command line.
         Once loaded, it looks like this:
         
         ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
         A) USER:  NODE MAIL                                      RECORD:     5
         ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
         B) Packet type:         QWK           L) Abort if no msgs:    Yes
         C) Update pointer:      Yes           M) Ask before send:     No
         D) Xfer protocol:       Z             N) Default msg select:  All msgs
         E) Msg to ALL as pers:  No            O) Turbokey:            On
         F) Display Menu:        No            P) Net Status:          Net node
         G) Archive choice:      ZIP           Q) Net identification:  NODE
         H) Last-on (YYMMDD):    921102        R) .MSG Date (YYMMDD):  800101
         I) Send own msgs:       No            S) .MSG Time (HHMMSS):  000000
         J) Send bulletins:      No            T) .MSG Length:         0
         K) Send new file info:  No
         ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
                 TO SELECT USER: Press , , PgUp, PgDn.  (<ESC> to QUIT)
         
                 OPTIONS:                   EDIT USER SHOWN:
                 1) Find User Name          A-T) Edit data above
                 2) Add new user            4)   Edit conf data
                 3) Purge User Records      5)   Delete user
         ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
         
         The above screen shows all of the user's settings, and each one can be
         changed as needed by pressing the letter corresponding to it (A-T).
         You can use the up, down, PgUp, PgDn keys to move forward and backward
         through the user file.  Press "5" to delete the user, or "4" to edit
         his/her conference selection settings.
         


     UTILITY PROGRAMS BUNDLED WITH MAIL MANAGER +PLUS+              - Page 85 -


         Additional numeric options (1-3) work as you would expect:
         
               1 - Find a user.  You'll be asked for a search string.
               2 - Add new user.  Adds a blank user record to the end of the
                   file.
               3 - Purge.  You will be asked to purge by date, etc.
               
         Options "A" through "O" pertain to the user's settings as they
         configured themselves from within Mail Manager +Plus+.
         
         The user has no control over options "P" through "T" from within the
         door.
         
         Options "P" and "Q" pertain to QWK network users.  Usage of this
         utility for network operation is described in NETINFO.DOC.
         
         Options "R", through "T" pertain to Mail Manager +Plus+ duplicate
         upload checking, and should not need to be modified.


     UTILITY PROGRAMS BUNDLED WITH MAIL MANAGER +PLUS+              - Page 86 -


         UPDATE AND UPDATUSR
         -------------------
         
         The pair of utilities UPDATE.EXE and UPDATUSR.EXE are intended as
         "one-shot" programs for SysOps who are upgrading from v1.30 through
         v1.35 of Mail Manager.  If you are not upgrading from one of these
         previous versions of Mail Manager, you do not need these two
         utilities.
         
         By the time you read this, you will likely have already converted your
         files, but here is the scenario anyway:
         
             - BACK UP YOUR ORIGINAL MAILMGR.CFG and MAILMGR.USR FILES!  (Just
             in case something goes wrong).
             
             - BOTH programs must be run from your Mail Manager directory.
             
             - UPDATE.EXE updates your binary configuration file (MAILMGR.CFG)
             to the new format used by Mail Manager +Plus+.
             
             - UPDATUSR.EXE updates Mail Manager's binary user file
             (MAILMGR.USR) to the new format used by Mail Manager +Plus+.
             
         These utilities are "run-once-then-throw-them-away".  Once your files
         are converted, you won't need them again.


    MAIL MANAGER +PLUS+ MENU COMMANDS                               - Page 87 -


         THE MAIN MENU
         -------------
         
         Although we hope that you'll find Mail Manager to be pretty self-
         explanatory, a complete run-down on everything that you can do with
         this door follows.
         
         A shorter version of this is available to the user, in the online help
         files MMGR1.HLP and MMGR2.HLP.
         
         The menu itself looks something like this:
         
               ---------------------------------------------
             /     MAIL MANAGER +PLUS+ MAIN MENU        /    \
           /                                          /        \
           l  C)onfigure MAIL MANAGER                 l        l
           l  D)ownload mail                          l        l
           l  E)xpedite!  (Download then exit to bbs) l        l
           l  G)oodbye                                l        l
           l  Q)uit (return to bbs)                   l        l
           l  H)elp!                                  l        l
           l  P)ost a message                         l        l
           l  R)ead messages by conference            l        l
           l  U)pload your replies.                   l        l
           l  W)ho's online to RBBS-PC?               l        l
           l  X)pert toggle (this menu on/off)        l        l
           -------------------------------------------------------------------.
                                   HHHHHH          "--------------------------"
                                   HHIIII
                                   HHIIII
         
           Your choice, Username <C,D,E,Q,H,M,W,U,X,?>?
         
         PLEASE NOTE:  Users of versions earlier than 3.10 will note that the
         option to select which messages to extract (i.e. set message pointers)
         has been moved from the main menu to the configuration menu.  If you
         have installed a customized menu, you should revise it to reflect
         this.
         
         MAIN MENU commands are as follows:
         
           C - Configure Mail Manager.
               
               Brings up a separate configuration menu for the user's personal
               options.  These options are discussed separately immediately
               after Main Menu Commands.
               
           D - Download new mail.
               
               Will find and extract all new mail from your selected
               conferences, in the format that you told Mail Manager to use
               (Text or QWK).  Mail Manager will then compress the file(s) in
               your selected file compression format.
               


    MAIL MANAGER +PLUS+ MENU COMMANDS                               - Page 88 -


               Unless your file protocol is set to N)one, Mail Manager will
               then send you the mail packet.  If your default protocol is set
               to N)one, you'll be asked for the transfer protocol of your
               choice.  If you choose "N", the file will not be sent to you,
               and you'll be returned to the main menu.  Otherwise Mail Manager
               will do its best to send a compressed version of the mail to you
               via your selected choice.
               
               Upon completion of the download operation in QWK mode, Mail
               Manager will then check for the existence of a REP file and
               process it if found.  This provides compatibility with bi-
               directional transfer protocols which can upload a REP while
               downloading a QWK.
               
           E - Expedite!
               
               Same as Download (above), except automatically exits Mail
               Manager when finished.
               
               If you have configured the door to drop DTR when G)oodbye is
               chosen, this option will drop DTR after the download to
               disconnect the caller upon exit, otherwise it will return the
               caller to the BBS.
               
           G - Goodbye
               
               Returns to BBS (same as Q)uit), unless you have configured the
               door to drop DTR.  If so, it will drop DTR on the user
               (disconnects most modems).
               
           Q - Quit (return to BBS)
               
               What can we say?  This takes the user back to your bbs.
               
           H (or '?') - Display help file
               
               Displays an abbreviated version of these command descriptions.
               
           I - Sysop Information
               
               This command is not shown in the online help file, is not
               displayed in the command prompt, and is not shown in the menu
               itself.
               
               Only those with sufficient security to read ALL messages will be
               able to activate this command.  Everyone else will get the
               familiar "Command not recognized".
               
               The purpose of this command is to assist you in debugging your
               setup, and it is covered in detail elsewhere in this manual
               under "DEBUGGING YOUR SETUP".
               


    MAIL MANAGER +PLUS+ MENU COMMANDS                               - Page 89 -


               R - Read messages.
               
               Allows users to read messages while online within the door.
               This can be useful for checking out a message or two before
               downloading a packet.  User will be asked for which conference
               to read whenever this option is chosen.
               
               If the user has sufficient security to post a message in the
               conference they select here, they will have the option to reply
               to messages that they read, and choose to quote or not quote the
               message that they are replying to.
               
               Mail Manager +Plus+'s read function itself is somewhat
               rudimentary; we did not try to duplicate RBBS-PC itself in this
               regard.  The user can choose to read all messages, or personal
               messages only, reading "forward" starting with a particular
               message number, or S)ince last read.
               
           P - Post a message
               
               A complement to the R)ead option, allows user to post a message
               while online within the door, and will allow them to select only
               the conferences in which they have sufficient security to post.
               
               Mail Manager +Plus+ is equipped with a line editor, similar in
               function to RBBS-PC's.  Message length will be limited to 8 less
               than the lines per message allowed in that area (as configured
               for Mail Manager) for normal "non-net-status" users.  The same
               line editor used in the P)ost function is used when R)eplying to
               a message while reading online.
               
           U - Upload your replies
               
               Works with QWK-compatible mail reader/repliers only. Your
               uploaded file is expected to be compatible with the .REP format
               used by popular mail readers such as SLMR.  Mail Manager will
               look for the REP packet after the upload and attempt to place
               your replies into the proper message bases.
               
               If your default protocol is set to N)one, you'll be asked for
               the protocol that you wish to use.  If you select N)one, you'll
               be returned to the main menu.
               
               If you're in local mode as the Sysop, place the .REP file in the
               \MAILMGR\LOCAL directory, and choose this option.  This is
               covered further in the section regarding "DEBUGGING YOUR SETUP".
               


    MAIL MANAGER +PLUS+ MENU COMMANDS                               - Page 90 -


           W - Who's online?
               
               Displays a list of who's online to all nodes of this RBBS-PC.
               (Much like RBBS's command of the same name).
               
               Those with sufficient security to read ALL messages will have
               the following displayed:
               
                   - User's name,
                   - City/State, and
                   - BPS rate.
               
                   If a node is inactive, the last user's information is
                   displayed, and will be reported as "Last call".
               
               All other users will have the following displayed:
               
                   - User's name, and
                   - baud rate.
               
               If a node is inactive, "Waiting for next caller" is displayed.
               
           X - Expert toggle
               
               Turns the main menu on or off.  (Much like RBBS's command of the
               same name).  This setting is saved for the user's next time into
               the door.
               
         


    MAIL MANAGER +PLUS+ MENU COMMANDS                               - Page 91 -


         CONFIGURATION MENU COMMANDS:
         ----------------------------
         
         The configuration menu allows the user to select personal options, and
         select or change conferences from which to extract new mail.
         
         You'll be presented with a screen that looks something like this:
         
         ----------------------------------------------------------------------
         Configuration options:
         
          A - Choose active conferences.
          X - Message selection menu.
          B - Download messages in Q)WK or T)ext format..........: Q
          C - Msgs addressed to ALL marked as personal (QWK only): No
          D - Extract ONLY your personal mail as default ........: No
          E - Extract messages written by YOU ...................: Yes
          F - Abort packet if no messages .......................: No
          G - Send updated bulletins ............................: Yes
          H - Send new file listings ............................: Yes
          I - Ask before sending packet .........................: No
          J - Type of file compression to use ...................: ZIP
          K - Default file transfer protocol ....................: Z
          L - Update high message numbers after downloading .....: Yes
          M - Update high message numbers after R)eading ........: Yes
          T - Use 'TurboKeys' (act on 1-character commands) .....: No
              -----------------------------
          ? - Display help file
          Q - Quit.  (Finished configuring)
         
          Enter your choice(s), UserName <A,B,C,D,E,F,G,H,I,J,K,L,M,Q,T,X,?> ->
         ----------------------------------------------------------------------
         


    MAIL MANAGER +PLUS+ MENU COMMANDS                               - Page 92 -


         Now let's see what these various commands do:
         
          A - Select conferences to extract and download.
         
               You'll be presented with a list of conferences that you are able
               to access, which will look something like this:
               
           --------------------------------------------------------------------
           You may select any conference which is shown in UPPER CASE.
           Conferences shown in lower case must first be joined from the bbs.
           Conferences you've marked as active are surrounded in brackets '[]'.
           Conferences marked as --- are not available.
           
                     1 - [MAIN   ] 11 -  TEEN     21 - [RSYS   ]
                     2 - [4SALE  ] 12 - [PRIVATE] 22 - [BITS   ]
                     3 - [MS-DOS ] 13 - [SYSOP  ] 23 - [POL    ]
                     4 -  BBS      14 - [USER   ] 24 - [CRES   ]
                     5 -   ---     15 -   grafx   25 - [WINB   ]
                     6 - [CODE   ] 16 -   arj     26 - [MAILMGR]
                     7 - [DEBATE ] 17 -   ---
                     8 - [HAM    ] 18 - [QB     ]
                     9 -  HUMOR    19 - [RBBS   ]
                    10 - [IBM    ] 20 - [DEV    ]
           
           Enter conference number(s) to toggle on/off, or [ENTER] to quit.
           ->
           --------------------------------------------------------------------
               
               NOTE:  If you have configured your board NOT to show
                  empty/unjoinable conferences, the line "Conferences marked as
                  --- are not available" will not be shown.
               
               In this example, all conferences that you have joined (or which
               you have configured to be joinable via the Mail Manager +Plus+
               door, are flagged as active, except BBS (conference 4), HUMOR
               (conference 9), and TEEN (conference 11).
               
               If you wanted to mark those three as active, you'd enter:
                          4 9 11
               at the above prompt.
               
               Conferences #5 and 17 are shown as unavailable, meaning that the
               user either has insufficient security to access them, or you
               (the Sysop) have "reserved" these conference numbers in the
               MAILCFG program, for future use.
               
               Conferences #15 and 16 are active conferences, which the user
               has not joined, and which the sysop has not configured to allow
               joining from within the door, as indicated by being shown in
               lower case.  To access these conferences the user must first
               join them from RBBS.
               


    MAIL MANAGER +PLUS+ MENU COMMANDS                               - Page 93 -


               X - Message selection menu (for active conferences).
               
               Mail Manager will normally download mail based on the last
               message that you've read in each conference.  Since you can read
               mail both online AND offline, and have the option of telling
               Mail Manager NOT to update your last message read markers, you
               might want to use this option to reset them to what you want.
               
               You can also use this option to set individual conferences to
               extract the type of mail that you're after.  Each conference can
               be configured in 1 of 3 different ways:
               
                  A)ll         - Extract all mail from this conference
                  P)ersonal    - Extract only your personal mail
                  S)ys Default - Extract based on what you told Mail Manager
                                 to do by default via option D on the
                                 Configuration menu (see below).
               
           B - Download messages in Q)WK or T)ext format
               
               Set to text if you want to use Mail Manager as a simple "extract
               and download" system (all messages in a single continuous ascii
               file).
               
               Set to QWK if you want to read and reply offline using a QWK-
               compatible mail reader.
               
                            <<< QWK NETWORK USERS >>>
                   
                   ** NOTE **  This field is different for QWK network users.
                   If you have given a user "net status" via MUSER, this gives
                   them the option of creating a "full QWK" (with all
                   accompanying files normally present within), or a minimized
                   QWK packet that contains only what is necessary for network
                   mail transfer.  The latter would save them archiving and
                   transfer time by creating a smaller packet, the former might
                   be preferred if they wish to review the packet via an
                   offline reader program, and can be useful for them to set up
                   the conference numbers appropriately on their end of the
                   line.
                   
                   At any rate, they will have the option one way or the other,
                   and can change it whenever they wish.
                   
           C - Msgs addressed to ALL marked as personal (QWK only)
               
               If set to "Y", Mail Manager will add messages addressed to "ALL"
               to the user's personal index the QWK packet.
               
               


    MAIL MANAGER +PLUS+ MENU COMMANDS                               - Page 94 -


           D - Extract ONLY your personal mail as default
               
               If set to "Y", Mail Manager will not extract a message unless it
               is addressed to you.  (Will also extract msgs addressed to "ALL"
               if you have option C set to "Y".)  This is the default setting
               for the user, but it can be overridden for individual
               conferences when setting the
               conference message pointers (see main menu option M).
               
           E - Extract messages written by you
               
               If set to "NO", Mail Manager will not include messages from you
               in your packet.
               
           F - Abort packet if no new messages
               
               You might not want to do this if you would still like to receive
               new file listings or updated system news or bulletins.
               
           G - Send updated bulletins
               
               If set to "No", any updated bulletins which the sysop has
               designated as mandatory will still be included.
               
           H - Send new file listings
               
               If you select this option, a listing of newly-uploaded files
               will be included in your mail packet.
               
               This option is only operational on systems with standard RBBS
               FMS style file listings.
               
           I - Ask before sending packet
               
               If set to "Yes", will cause Mail Manager to prompt you whether
               or not you want to receive the mail packet that it just created
               for you.  Will otherwise go right into the download when
               finished extracting.
               
           J - Type of file compression to use
               
               If the Sysop has activated this option, you can choose from the
               file compression utilities offered on this system (ZIP, ARC,
               etc.).
               
           K - Default file transfer protocol
               
               Choose from the protocols offered by your sysop (Xmodem, Zmodem,
               etc.).  If set to N)one, Mail Manager will prompt you for which
               protocol to use at each file transfer.
               


    MAIL MANAGER +PLUS+ MENU COMMANDS                               - Page 95 -


               L - Update high message numbers after downloading
               
               If this is set to NO, both RBBS and Mail Manager will think that
               you haven't read the messages that you've downloaded. (Mail
               Manager will extract them again your next time in).
               
           M - Update high message numbers after R)eading
               
               If set to NO, any messages that you read in the door will still
               be downloaded in your next mail packet.  This can be handy for
               checking a message or two before downloading your mail.
               
               If set to YES, the highest message number you read sets your
               high message marker, and only higher message numbers  will be
               included in your next mail packet.
               
           T - Use 'TurboKeys' (act on 1-character commands)
               
               Works like RBBS-PC's toggle of the same name.  If set to Yes,
               Mail Manager will not wait for [ENTER] when asking you for
               input.
               
           ? - Display help file
               
               Display help file which explains the configuration options.
               
           Q - Quit (finished configuring)
               
               (Or just press [ENTER] to accomplish the same thing).


     APPENDIX A - COMMON PROBLEMS                                   - Page 96 -
     

         
         Problem :  Not finding the Sysop in any conferences.
                    
         Solution:  Double-check your setting of "Remote Sysop Name" on the
                    first screen of the MAILCFG program.  This setting must be
                    the name that you use to log onto your system remotely, NOT
                    your name as you are known to your users.
                    
         ----------------------------------------------------------------------
                    
         Problem :  Shows "Error finding new message" when trying to extract
                    your first mail packet.
                    
         Solution:  Run MAILFIX.EXE against the message base in question (using
                    the proper command line switches).  Re-read the section of
                    this document entitled "Before you begin".
                    
         ----------------------------------------------------------------------
                    
         Problem :  Always showing Sysop name when operating remotely.
                    
         Solution:  Probably not copying the correct DORINFOx.DEF file to the
                    Mail Manager directory prior to loading the door.  Drop to
                    DOS, and take a look at the DORINFOx.DEF that was in use at
                    the time.
                    
                    Also possible that the door is coming up in local mode.
                    Check your DOORS.DEF and MAILMGR.BAT files to be sure they
                    are set correctly.  Mail Manager should be called (as a
                    minimum) like so:
                    
                        MAILMGR %1
                    
                    (Where %1 is the node number).  If you suspect that it is
                    NOT being passed correctly, turn ECHO ON at the top of your
                    batch file and watch what it actually passed to the door.
                    
         ----------------------------------------------------------------------
                    
         Problem :  Always using locked BPS rate for download estimates,
                    instead of true connect rate.
                    
         Solution:  No fix if you are running stock RBBS-PC v17.3C and lower.
                    You must upgrade to RBBS-PC v17.4 to get this figure
                    reported correctly, or recompile RBBS-PC with the CBAUD
                    merge.
                    
                    If you are running RBBS-PC v17.4 and above, change your
                    DOORS.DEF line to read something like:
                    
                       MAILMGR,5,,D,"C:\MAILMGR.BAT [NODE] [CBAUD]",N,,
                    
                    Then, in MAILMGR.BAT, change the line that calls Mail
                    Manager to read:  MAILMGR %1 /CBAUD%2
                    


     APPENDIX A - COMMON PROBLEMS                                   - Page 97 -


         ----------------------------------------------------------------------

         Problem :  Not allowing REP uploads to a particular conference, with
                    the error message "Message base full".
                    
         Solution:  Make 100% sure that both RBBS-PC and Mail Manager +Plus+
                    are configured to the exact same type of message base.  For
                    instance, if RBBS-PC is configured to have message base
                    "grow" as messages are added, yet that conference is
                    configured in Mail Manager +Plus+ as fixed length, this
                    type of error will appear EVERY time a message is uploaded
                    for that conference.

                    If all appears to be sound, and that error message still
                    appears, try running MAILFIX.EXE against the offending
                    message base.

         ----------------------------------------------------------------------

         Problem :  Program gives error message "Unable to pack...", after
                    trying to compress a mail packet.

         Solution:  We have heard this one before, (and have run into it
                    ourselves), and it has always been one of three things:

                    - Your file compression program was not where the list of
                       archivers said it was (MAILMGR.ARL), or

                    - There was insufficient memory to run the archiver, or

                    - There was insufficient disk space to archive the mail
                      packet for the user.  (A 1,000-message packet can be over
                      1 meg in size before compression).

                    Read the section of this document entitled "CHECKLIST OF
                    REQUIREMENTS" for Mail Manager +Plus+ memory requirements.

         ----------------------------------------------------------------------

         Problem :  Program gives errors while extracting mail from a FIDO
                    *.MSG area, and/or has problems when updating last message
                    read in a FIDO area after a download.

         Solution:  More than likely, Mail Manager +Plus+ experienced an error
                    with the index file for that FIDO area that it wasn't able
                    to recover from.  Try running the MMINDEX.EXE program, and
                    insure that MMINDEX is in your nightly event as the LAST
                    thing before your BBS comes back up.

         ----------------------------------------------------------------------


     APPENDIX A - COMMON PROBLEMS                                   - Page 98 -
     

         Problem :  Local screen looks fine, but the caller on the remote end
                    of the line has incomplete and partially garbled screens.
                    
         Solution:  If your communications port is locked higher than the
                    user's true connect speed (typically 19200 or 38400 for
                    today's fast modems), Mail Manager +Plus+ is probably
                    overrunning the communications buffer.  You can get around
                    this problem by installing a FOSSIL driver such as BNU or
                    X00 (available on bulletin boards all over the place), and
                    telling Mail Manager +Plus+ to always use the FOSSIL for
                    flow control.  Set the flow control option (in the MAILCFG
                    program) to "F".
                    
                    See the section of this document entitled "IF YOU HAVE A
                    LOCKED BPS RATE" for more information on this subject.
                    
         ---------------------------------------------------------------------
                    
         Problem :  Mail Manager +Plus+ is not finding some of the files as set
                    in the configuration file, or always seems to be using
                    defaults instead of the options that you have custom-
                    configured.
         
         Solution:  The most likely cause of this problem is an incomplete (or
                    incorrect) drive:\path\file designation for a key file or
                    two in the configuration program.  In particular - DO NOT
                    simply use a "drive:filename.ext" designation to tell Mail
                    Manager +Plus+ where to look.  Mail Manager +Plus+ always
                    operates out of a work directory, and is never going to be
                    in the \MAILMGR directory when it looks for its files.  For
                    example:
                    
                        D:PROTO.DEF
                    
                    may not work, but:
                    
                        D:\MAILMGR\PROTO.DEF
                    
                    might.
         


     APPENDIX B - CONTACTING THE AUTHORS                            - Page 99 -


         Up through this release, Mail Manager +Plus+ has been a joint effort
         of Chip Morrow and Doug Wilson (SysOp and Co-SysOp of Mail Manager's
         original home bbs).  Personal time commitments are forcing Chip
         Morrow's withdrawal from future Mail Manager development and his
         closing of Mail Manager's home bbs, but Doug Wilson is continuing
         under the new banner of Makai Software.  For the time being, we both
         will continue to provide support.  Comments, ideas, suggestions, and
         whatever else you want to throw our way are always appreciated and
         should be directed to any of the following:
         
         Good ole' US Mail:
                             Makai Software
                             870 Golden Drive
                             Newark, OH 43055
                             
         Bulletin boards:
         
            Three RBBS-PC boards have agreed to jump in as official Support
            Sites in the wake of the closing of Mail Manager's original home
            board.  All three have the latest versions of Mail Manager, Mail
            Manager +Plus+, MailFix, MNET, and any other RBBS-related software
            we may develop.  The sysops have committed to making these files
            available to first time callers, bypassing the usual new user
            registration hassles, when they log on with the special
            username/password combinations shown below:
            
            Board:        BRODMANN'S PLACE   HOTLine Co-op   THE DOG HOUSE
            Location:     Waldorf, MD        Monroe, LA      Kings Beach, CA
            Sysop:        Dave Brodmann      Eddie Rowe      Kip Gies
            Phone:        301-843-5732       318-345-1955    916-546-7002
            Modem:        HST/v.32bis        v.32bis         v.32bis
            Username:     FREE GUEST         HOTLINE BBS     MAILMGR LATEST
            Password:     USER               GUEST           VERSION
            Net Address:  Fido 1:109/806     Fido 1:380/14   RBBS 8:919/20
                          Rime ->BRODMANN
            
            In addition, a local (to us) BBS that we both check into on a near-
            daily basis is:
               
               THE MOTHER BOARD (WildCat!)
               Buckeye Lake, OH
               Michael Graham, Sysop
               Data line: 614-928-2259
               Modem: HST/v.32bis
               Fido: 1:226/1400 <- Yep, that IS Newark Connection's
                                   old address - it's not a typo.
               
               Fido netmail sent to The Mother Board or messages left there
               directly will probably get the fastest response.
               
               PLEASE NOTE: as this is written, 1:226/1400 is NOT set up to
               handle MMGR/MNET file requests, although these files will be
               available there for download.
            


    APPENDIX B - CONTACTING THE AUTHORS                            - Page 100 -


            We check into all of these boards on a regular (but not necessarity
            daily) basis, and will answer questions left on or netmailed to any
            of them.  The Mother Board, being a local call, gets the most
            attention and is probably the place to get the fastest response.
            Please leave messages as PUBLIC so that whichever of us calls first
            will be able to see them.  The sysops of the three Support Boards
            are all experienced with Mail Manager, and may be able to handle
            some of your questions without help from Chip or me.
            
         Computer network conferences:
            
            We will also continue to monitor the following computer network
            conferences.  If you don't have access to Fido netmail, these may
            be your best bet for obtaining support in a timely fashion:
            
                                RIME:  RBBS-PC and RBBSQWK
                                FIDO:  RBBS-PC and OFFLINE
                                               
         We're sorry, but we simply do not have the time or resources to make
         voice calls to help with debugging your individual Mail Manager setup.
         On the other hand, we'd like to see you in any of the above echo
         conferences, where you can get help from others as well as ourselves,
         and where questions/answers/reports/release notices get a much wider
         audience, and can benefit more people.


    APPENDIX C - ACKNOWLEDGEMENTS                                  - Page 101 -


         Microsoft, Crescent Software, DSZ, PKZIP, LHARC, ARJ, LZEXE, PKLITE,
         JIMMER, TQM, LANtastic, DESQview, BNU, X00, RBBSMAIL, MSGTOSS,
         OVERMAIL, PDQ, PDQCOMM, QuickBASIC, RBBS-PC, SLMR, JABBER, OFFLINE,
         OLX, RNET, TNET, and SHROOM (did we miss any?) are all trademarks or
         tradenames of their respective authors and/or companies, and are
         mentioned throughout our documentation for clarity only.
         
         Our Special thanks go to everyone who supported us through development
         of the original Mail Manager package.  Many of the names have faded,
         some have gone on to other BBS's and/or other doors, others have grown
         silent over the last few years, others continue to provide us with
         suggestions to this day.  Without your support, the door would never
         be where it is today.  Some names of special note:
         
            Michael Lurie, who has supported the door (and its continued
            development) since day one, and who continues to be cheerfully used
            and abused by pre-release copies.
            
            Dave Brodmann, who was severely subjected to beta versions of the
            standard Mail Manager package containing "+Plus+" features.  Dave
            definitely helped to make our shareware effort a reality,
            especially the > 250 conference support.
            
            The trio of Rod Bowman, Don Smith, and Joe Tailleur who beta tested
            the first versions to support FIDO *.MSG's and helped solve a lot
            of early problems before Mail Manager +Plus+ hit the streets.
            
            Kip Gies, who tested a late beta of v2.03 and helped us get the
            initial bugs out of the FIDO *.MSG handling.
            
            Eddie Rowe, who tested the last betas of pre-v3.x code, helped us
            get some last-minute bugs out of the new code, found the "old
            format" problem in outbound mail packets created by v2.x, and
            provided us with updated Fido format documentation.
            
            Marion Royal, who ran our QWK network implementation through the
            wringer, picked MNET and MUSER apart <g>, and provided us with
            sufficient information to implement QWK network capability.  There
            would be no QWK networking in this door without Marion's efforts.
            
            Paul Di Novo, who verified that the door really could work in a
            non-RBBS-PC environment, and provided us with useful information
            for future compatibility issues.
            
         I must express my sincere appreciation to CHIP MORROW, who poured his
         heart and soul into this project for over two years, and who has been
         an absolute joy to work with.  Without Chip, Mail Manager would not
         exist.  Period.  If there is anyone who better exemplifies the Spirit
         of RBBS as defined by Tom Mack than Chip, I'm sure I haven't met him.
         
         And thanks to everyone else who commented and offered suggestions,
         help, and beta testing.  We honestly cannot remember all of the names,
         and do apologize for that!
         


    APPENDIX D - MAIL MANAGER'S FILE FORMATS                       - Page 102 -


         Just in case someone out there has an inkling to write a utility
         program or two for use with their Mail Manager +Plus+ setup, here are
         the formats for the Mail Manager +Plus+ v3.10 binary system files,
         MAILMGR.CFG and MAILMGR.USR.
         
         +--------------------------------------------------------------------+
         | MAILMGR.USR - Mail Manager's internal users file.                  |
         |               One 570-byte record per user.  Each 570-byte record  |
         |               broken down as follows:                              |
         |--------------------------------------------------------------------|
         | Start Stop Length Record Type Description                          |
         |====================================================================|
         |     1   31     31    STRING   The user's name, in upper case,      |
         |                               left-justified, padded with ASCII 32s|
         |--------------------------------------------------------------------|
         |    32  531    500    STRING   Bit-mapped conference flags for each |
         |                               user, 1 byte per conference.  If bit |
         |                               is set to 1 it means:                |
         |                                Bit: 0 = conf active                |
         |                                     1 = accept default msg select. |
         |                                     2 = if bit 1 not set, pers only|
         |                                     3 = conf net status granted    |
         |                                     4 = if bit 3 set, net access to|
         |                                         private messages.          |
         |                                 5,6,7 = reserved                   |
         |--------------------------------------------------------------------|
         |   532  532      1    STRING   User's QWK preference.  Either "Q"   |
         |                               or "T".  (QWK or TEXT).              |
         |--------------------------------------------------------------------|
         |   533  533      1    STRING   User's flag for whether or not to    |
         |                               update last message read in the RBBS |
         |                               user files (after downloading pkts). |
         |                               ASCII 1 for true, 255 for false.     |
         |--------------------------------------------------------------------|
         |   534  534      1    STRING   Letter of the user's default file    |
         |                               protocol choice, in upper case.      |
         |--------------------------------------------------------------------|
         |   535  535      1    STRING   Messages addressed to "ALL" marked   |
         |                               as personal in QWK packet?  ASCII 1  |
         |                               for true, 255 for false.             |
         |--------------------------------------------------------------------|
         |   536  536      1    STRING   Xpert toggle on or off (ASCII 1, 255)|
         |--------------------------------------------------------------------|
         |   537  537      1    STRING   Bit flag byte for other user options.|
         |                                          Bit:  0 = Send own msgs   |
         |                                                1 = Send bullets    |
         |                                                2 = Send newfiles   |
         |                                                3 = Abort if no msgs|
         |                                                4 = Ask before send |
         |                                                5 = Only pers mail  |
         |                                                6 = Turbokey toggle |
         |--------------------------------------------------------------------|
         |   538  540      3    STRING   User's choice of archiver (ZIP, ARC, |
         |                               etc.)                                |
         |--------------------------------------------------------------------|


    APPENDIX D - MAIL MANAGER'S FILE FORMATS                       - Page 103 -


         |   541  546      6    STRING   "YYMMDD" that user last used the     |
         |                               door. ("911223" = 23 Dec 91)         |
         |--------------------------------------------------------------------|
         |   547  547      1    STRING   Net status CHR$(0=none,1=node,2=host)|
         |--------------------------------------------------------------------|
         |   548  555      8    STRING   Packet name for net status user      |
         |--------------------------------------------------------------------|
         |   556  559      4      LONG   Date/Time of last REP packet         |
         |--------------------------------------------------------------------|
         |   560  563      4      LONG   FileSize of last REP packet          |
         |--------------------------------------------------------------------|
         |   564  564      1    STRING   Update last read after reading online|
         |                               CHR$(1) = true, 255 = false.         |
         |--------------------------------------------------------------------|
         |   565  570     24    STRING   Reserved for future use.             |
         +--------------------------------------------------------------------+
         
         +--------------------------------------------------------------------+
         | MAILMGR.CFG- Mail Manager's configuration file.                    |
         |              Consists of one 556-byte header, followed by a number |
         |              of 384-byte conference configuration records.         |
         |                                                                    |
         |                          HEADER RECORD:                            |
         |--------------------------------------------------------------------|
         | Start Stop Length Record Type Description                          |
         |====================================================================|
         |     1   35     35   STRING    Name of the BBS (in proper case).    |
         |--------------------------------------------------------------------|
         |    36   66     31   STRING    Remote logon name of the sysop (left-|
         |                               justified, in upper case, padded with|
         |                               ASCII 32 blanks).                    |
         |--------------------------------------------------------------------|
         |    67   81     15   STRING    Sysop's public first name.           |
         |--------------------------------------------------------------------|
         |    82   96     15   STRING    Sysop's public last name.            |
         |--------------------------------------------------------------------|
         |    97   98      2  INTEGER    Security level to read ALL messages. |
         |--------------------------------------------------------------------|
         |    99  100      2  INTEGER    Security level to use in local mode. |
         |--------------------------------------------------------------------|
         |   101  102      2  INTEGER    Local sysop's graphic preference.    |
         |                               2 = ANSI, 1 = ASCII, 0 = None.       |
         |--------------------------------------------------------------------|
         |   103  163     61   STRING    Default tagline for all conferences. |
         |--------------------------------------------------------------------|
         |   164  165      2  INTEGER    Number of 334-byte conference        |
         |                               configuration records that follow    |
         |                               this header record.                  |
         |--------------------------------------------------------------------|
         |   166  173      8   STRING    First 8 characters of extract file   |
         |                               name to use (this is the "*" of      |
         |                               *.QWK, *.REP, *.ZIP, etc.).          |
         |--------------------------------------------------------------------|


    APPENDIX D - MAIL MANAGER'S FILE FORMATS                       - Page 104 -


         |   174  176      3   STRING    3 upper case characters designating  |
         |                               the default file compression type    |
         |                               (ZIP, ARC, ARJ, or LZH)              |
         |--------------------------------------------------------------------|
         |   177  216     40   STRING    Full path/filename of the NEWS file. |
         |--------------------------------------------------------------------|
         |   217  256     40   STRING    Full path/filename of the list of    |
         |                               bulletins (MAILMGR.BUL).             |
         |--------------------------------------------------------------------|
         |   257  257      1   STRING    Network type to use in local mode.   |
         |                               D)os, N)etbios, desQ)view.           |
         |--------------------------------------------------------------------|
         |   258  258      1   STRING    Handshake method to use, upper case. |
         |                               R)ts, X)on, N)one, or F)ossil.       |
         |--------------------------------------------------------------------|
         |   259  260      2  INTEGER    Version number (3.10 = 310).         |
         |--------------------------------------------------------------------|
         |   261  300     40   STRING    Path/filename of MAILMGR.PRO         |
         |--------------------------------------------------------------------|
         |   301  340     40   STRING    Path/filename of FMS directory.      |
         |--------------------------------------------------------------------|
         |   341  380     40   STRING    Path/name of list of archivers.      |
         |--------------------------------------------------------------------|
         |   381  395     15   STRING    Name of environment variable to      |
         |                               path/name of XFER-x.DEF log file.    |
         |--------------------------------------------------------------------|
         |   396  396      1   STRING    Modify uploaded messages date & time |
         |                               stamp to the current system time?    |
         |                               (Y or N)                             |
         |--------------------------------------------------------------------|
         |   397   427     31  STRING    City/State where BBS is located.     |
         |--------------------------------------------------------------------|
         |   428   439     12  STRING    Phone number of BBS. "xxx-xxx-xxxx"  |
         |--------------------------------------------------------------------|
         |   440   440      1  STRING    SmartText ID character               |
         |--------------------------------------------------------------------|
         |   441   480     40  STRING    Default path to *M.DEF conferences.  |
         |--------------------------------------------------------------------|
         |   481   520     40  STRING    Path/name of echo toss log.          |
         |--------------------------------------------------------------------|
         |   521   525      5  STRING    Start of timelock (HH:MM).           |
         |--------------------------------------------------------------------|
         |   526   530      5  STRING    End of timelock (HH:MM) - 24 hour    |
         |                               format for both of these.            |
         |--------------------------------------------------------------------|
         |   531   531      1  STRING    Drop DTR on G)oodbye/E)xpedite? (Y/N)|
         |--------------------------------------------------------------------|
         |   532   532      1  STRING    Show empty/unjoinable confs? (Y/N)   |
         |--------------------------------------------------------------------|
         |   533   556     24  STRING    Reserved for future use.             |
         +--------------------------------------------------------------------+
         


    APPENDIX D - MAIL MANAGER'S FILE FORMATS                       - Page 105 -


         +--------------------------------------------------------------------+
         |                   CONFERENCE CONFIGURATION RECORD:                 |
         |--------------------------------------------------------------------|
         | Start Stop Length Record Type Description                          |
         |====================================================================|
         |     1    7      7   STRING    Name of the conference, upper case.  |
         |--------------------------------------------------------------------|
         |     8    8      1   STRING    # of lines per msg (CHR$ byte value  |
         |                               plus 32).  CHR$(131) = 99 lines per  |
         |                               message.  CHR(0) = do not split long |
         |                               messages.                            |
         |--------------------------------------------------------------------|
         |     9   25     17   STRING    Reserved for future use.             |
         |--------------------------------------------------------------------|
         |    26  105     80   STRING    Path/name to USERS file.             |
         |--------------------------------------------------------------------|
         |   106  185     80   STRING    Path/name to MESSAGES file.          |
         |--------------------------------------------------------------------|
         |   186  186      1   STRING    Allow ANSI in REPs?  (Y, N)          |
         |--------------------------------------------------------------------|
         |   187  187      1   STRING    Allow high/low ASCII in REPs? (Y, N) |
         |--------------------------------------------------------------------|
         |   188  189      2  INTEGER    Security level needed to join.       |
         |--------------------------------------------------------------------|
         |   190  191      2  INTEGER    Security level needed to post.       |
         |--------------------------------------------------------------------|
         |   192  252     61   STRING    Tagline for this conference.         |
         |--------------------------------------------------------------------|
         |   253  253      1   STRING    Fido-style tearlines?  (Y, N)        |
         |--------------------------------------------------------------------|
         |   254  254      1   STRING    Type of message base? (Y, N, F)      |
         |--------------------------------------------------------------------|
         |   255  255      1   STRING    Allow join within door? (Y, N)       |
         |--------------------------------------------------------------------|
         |   256  335     80   STRING    Path/Name of conf alias file.        |
         |--------------------------------------------------------------------|
         |   336  337      2  INTEGER    Zone ID (for FIDO areas)             |
         |--------------------------------------------------------------------|
         |   338  339      2  INTEGER    Net ID  (for FIDO areas)             |
         |--------------------------------------------------------------------|
         |   340  341      2  INTEGER    Node ID (for FIDO areas)             |
         |--------------------------------------------------------------------|
         |   342  342      1   STRING    Netmail area?  (Y, N).               |
         |--------------------------------------------------------------------|
         |   343  343      1   STRING    Add tear/tag to end of FIDO msg?(Y,N)|
         |--------------------------------------------------------------------|
         |   344  358     15   STRING    Symbolic area name for this FIDO     |
         |                               conference. (Optional)               |
         |--------------------------------------------------------------------|
         |   359  359      1   STRING    Allow uploaded messages to be marked |
         |                               as private in this conf?  (Y, N)     |
         |--------------------------------------------------------------------|
         |   360  384     25   STRING    Long Description of the conference.  |
         +--------------------------------------------------------------------+

    APPENDIX E - ABOUT THIS DOCUMENT                               - Page 106 -
         Programmers have long been known to be terrible about writing
         documentation to cover their own software, and we are probably not
         going to disprove this theory with the opus you are reading now.
         
         After two years of threatening to do so, we have finally taken the
         rambling mess which spewed out of a couple of different text editors
         (the same ones we used to do the program coding) and shoved it all
         into an actual-by-gum word processor <gasp> to try to get more
         consistency of formatting, automatic page numbering, etc.
         
         But the basic text is what you have all come to love (?) in previous
         releases.  This means that there are two constants:
         
         - It SHOULD print out just fine on standard tractor-fed 8 1/2 x 11
         paper on your garden-variety dot-matrix printer.  We have attempted to
         limit page length to 60 lines, to allow it to be printed on 60-line-
         per-page laser printers.
         
         - It is practically guaranteed to contain spelling and grammar errors.
         
         This thing is probably too long by half, but every time we try to cut
         it down, we end up adding more than we cut (sounds sort of like
         Congress trying to trim the Federal Budget...)
         
         
                    Sincere Best Wishes to Each of You,
         
                    Doug Wilson