******************************
                         *                            *
                         *      DOUBLE DIRECTORY      *
                         *                            *
                         *        Version 1.40        *
                         * Copyright 1991, 1992, 1993 *
                         *      by George Tylutki     *
                         *                            *
                         ******************************

                _______
           ____|__     |               (R)
        --|       |    |-------------------          100% Cotton Software
          |   ____|__  |  Association of             RR 1 Box 1622
          |  |       |_|  Shareware                  Hop Bottom, PA 18824
          |__|   o   |    Professionals              717-289-4019
        -----|   |   |---------------------
             |___|___|    MEMBER


                                ================
                                  Introduction
                                ================

        Double Directory displays two disk directories side-by-side.
        Either can be the source or destination for copying, moving,
        renaming, deleting, viewing and printing files.  It can compare
        two directories and tag the differences.  Both directories can be
        scrolled simultaneously.  There are also functions for changing
        the attributes of files and sorting, making, masking and removing
        directories.  Individual files and entire directories can be
        tagged for moving, deleting, etc.  The user can shell to DOS,
        shell and run a program (normal), and shell and run a program
        with Double Directory removed from memory.  Double Directory's
        point-and-shoot interface makes it easy to tag files and navigate
        subdirectories.  The display colors can be changed and several
        other options can be configured.  With an EGA or VGA, more files
        can be displayed in the 43- and 50-row modes.  Double Directory
        is fast and easy to use: the commands are mnemonic and can be
        accessed via menus, function keys or hot keys.  It has context-
        sensitive help.  The manual is comprehensive with a complete
        index.

        After the table of contents, you will find installation,
        registration, warranty and support information.  This is followed
        by a general introduction to Double Directory and a reference
        section for each function.  At the end there is a table of keys
        (quick reference chart), a list of error messages, a complete
        index and a registration form.  There is also a section of TIPS
        which can help make Double Directory easier or faster to use.
        Throughout there are some Technical Notes that you do not have to
        read, but you might find interesting and/or useful.





                              =====================
                                Table of Contents
                              =====================


        Introduction . . . . . . . . 1         Directory Functions  . . 18
        Installation . . . . . . . . 3            Path  . . . . . . . . 18
           Minimum Requirements  . . 3            Mask  . . . . . . . . 19
           Installation. . . . . . . 3            Compare . . . . . . . 19
           Running Double Directory. 3            Sort  . . . . . . . . 20
           On-Line Help  . . . . . . 3            Reread  . . . . . . . 21
           Reading the Docs  . . . . 4            Tag . . . . . . . . . 21
           Printing the Docs . . . . 4            Make  . . . . . . . . 21
           Running Under Windows . . 4            Remove  . . . . . . . 21
           What's New? . . . . . . . 5            Information . . . . . 22
        What Is Shareware? . . . . . 5         Options Functions  . . . 22
        What Is ASP? . . . . . . . . 6            Sound . . . . . . . . 22
        Why Should I Register? . . . 6            Confirm . . . . . . . 22
        Warranty/License/Support . . 7            Rows  . . . . . . . . 22
        Using Double Directory . . . 8            Directory . . . . . . 23
           Getting Help . . . . . .  8            View  . . . . . . . . 24
           The Screen . . . . . . .  9            Color . . . . . . . . 26
           Moving Around the Screen  10           Path  . . . . . . . . 28
        Executing Commands  . . . . 10            Write . . . . . . . . 28
           F10, / . . . . . . . . . 10      Command-line Parameters . . 29
           Esc  . . . . . . . . . . 11      Miscellaneous . . . . . . . 30
           Shift-F10  . . . . . . . 11            Viruses . . . . . . . 30
           Enter  . . . . . . . . . 11            Windows Updating  . . 30
           Tagging Files  . . . . . 11            Memory Requirements . 30
           Entering Text  . . . . . 12            Necessary Stuff . . . 31
        Functions Reference . . . . 12      Tips . . . . . . . . . . .  31
           Main Menu  . . . . . . . 12      Keystrokes  . . . . . . . . 35
           File Functions . . . . . 13      Error Messages  . . . . . . 36
              Delete  . . . . . . . 13      Index . . . . . . . . . . . 39
              Rename  . . . . . . . 13      Registration Form . . . . . 44
              Copy  . . . . . . . . 14
              View  . . . . . . . . 14
              Move  . . . . . . . . 15
              Tag . . . . . . . . . 15
              Attributes  . . . . . 15
              DOS . . . . . . . . . 16
                 Shell  . . . . . . 16
                 Shell and run  . . 17
                 Clear and run  . . 17
                 Exit and run . . . 18
              Exit  . . . . . . . . 18

                                                Double Directory  3

                                ================
                                  INSTALLATION
                                ================

        ------------------------
          MINIMUM REQUIREMENTS    Double Directory requires: 1 or more
        ------------------------  disk drives; DOS 2.0  (DOS 3.0 or later
        recommended); any standard display device (MDA, Hercules, CGA,
        EGA, VGA); 272K (see "Memory Requirements" below).  Double
        Directory runs without problems under Microsoft Windows in
        Standard and Enhanced modes.

        ----------------
          INSTALLATION    Double Directory requires no special
        ----------------  installation.  Simply copy the various files
        (see PACKING.LST for a list of files and a description of each)
        to the disk or subdirectory where you want them and run Double
        Directory.  For example, if the Double Directory files are on a
        disk in drive a and you want to put them into an existing
        subdirectory on your hard disk (c) called "tools", then at the
        DOS prompt you would type "copy a:\*.* c:\tools\" and press the
        Enter key.  If you want to make a new subdirectory on your hard
        disk for Double Directory, look up "mkdir" in your DOS manual.

        After you become familiar with Double Directory, you can delete
        all of the files except DBLDIR.EXE (but see "On-line Help"
        below).  Double Directory is easy to use, however, you should
        read REGISTER.DOC or the section "Warranty/License/Support" in
        this manual.

        ----------------------------
          RUNNING DOUBLE DIRECTORY    The only file required to run
        ----------------------------  Double Directory is DBLDIR.EXE.
        First, log to the drive or subdirectory where Double Directory is
        located.  For example, if it is on a disk in drive a, then at the
        DOS prompt type "a:\" and press the Enter key.  Or if it is in
        the subdirectory "tools" on your hard drive, then at the DOS
        prompt, type "cd c:\tools" and press the Enter key.  Then, at the
        DOS prompt, type "dbldir" and press the Enter key to run Double
        Directory.  If you want to be able to run Double Directory from
        anywhere on your hard disk, look up "path=" in your DOS manual.

        ----------------
          ON-LINE HELP    If you want on-line, context-sensitive help
        ----------------  while running Double Directory, then the file
        DBLDIR.HLP must be in the same directory as DBLDIR.EXE.  If you
        get the message "Context-sensitive help not available" when you
        press F1 for help, read the sections "OPTIONS/PATH" and "Error
        messages: Context-sensitive help not available" in this manual.


                                                Double Directory  4

        -----------------------------
          READING THE DOCUMENTATION    You can read any of the
        -----------------------------  documentation files with a text
        editor or word processing program.  You can also use Double
        Directory to read the documentation.  For example, to read this
        manual,
        1. Run Double Directory.
        2. Press any key at the registration screen.
        3. Press "C" at the title screen (for Continue).
        4. When the directories have been displayed, use the cursor keys
           and Enter key to change to the disk or subdirectory which
           contains DBLDIR.DOC.
        5. Use the cursor keys to place the cursor bar on DBLDIR.DOC.
        6. Press the Ins key or the spacebar (to tag DBLDIR.DOC).
        7. Press "W" (to view the file).
        8. Press "Y" (Yes).
        9. Use the cursor keys to scroll through the file.

        ------------------------------
          PRINTING THE DOCUMENTATION    You can print any of the
        ------------------------------  documentation files with any text
        editor or word processing program.  You can also use Double
        Directory to print the documentation.  For example, to print this
        manual,
        1. While viewing the file (steps 1 to 8 above), press "V" (view
           options).
        2. Press "P" (print).
        3. Press "E" or "P" (print part or entire file).

        --------------------------------------------
          DOUBLE DIRECTORY UNDER MICROSOFT WINDOWS    To run Double
        --------------------------------------------  Directory under
        Microsoft Windows in Standard and Enhanced Modes, do the
        following:
         1. With Windows' Program Manager running, highlight an icon in
            the group in which you want to place Double Directory.
         2. Choose the Program Manager "File" menu.
         3. Choose "New".
         4. Choose "Program Item".
         5. Choose "Browse".
         6. Locate and highlight DBLDIR.EXE.
         7. Click "OK" several times until you are back to the desktop
            and there is a generic Microsoft icon for Double Directory in
            the group.
         8. Highlight the generic Double Directory icon.
         9. Choose the Program Manager "File" menu.
        10. Choose "Properties".
        11. Choose "Change Icon".
        12. Choose "Browse".
        13. Locate and highlight DBLDIR.ICO.
        14. Click "OK" several times until you are back to the desktop;
            you should see the Double Directory icon in the group.


                                                Double Directory  5


        -------------------------------
          WHAT'S NEW IN VERSION 1.40?    We are now members of the
        -------------------------------  Association of Shareware
        Professionals which means that you can be assured of product
        quality and support.  A problem with the Shell and Run function
        was fixed: sometimes you couldn't enter a complete command line.
        There is a new Toggle All function which toggles all on-tags in a
        directory off and all off-tags on.  View/Print now cancels more
        quickly and handles printer problems better.  The Options/Colors
        choices are more flexible and complete.  The active directory
        window is now highlighted in an additional way.  The manual has
        been revised so as to make some explanations clearer.  An icon is
        now included for running Double Directory under Microsoft
        Windows.

                             ======================
                               What is Shareware?
                             ======================

        SHAREWARE IS A DISTRIBUTION METHOD, NOT A TYPE OF SOFTWARE.
        Shareware distribution gives you a chance to try software before
        buying it.  If you try a Shareware program and continue using it,
        you are expected to register.  Individual programs differ on
        details: some request registration while others require it and
        some specify a maximum trial period.  The benefits of
        registration range from the basic right to continue using the
        software to an updated program with printed manual.

        Copyright laws apply to both Shareware and commercial software,
        and the copyright holder retains all rights, with a few specific
        exceptions as stated below.  Shareware authors are accomplished
        programmers, just like commercial authors, and their programs are
        of comparable quality.  The main difference is in the method of
        distribution.  The shareware author specifically grants the right
        to copy and distribute the software, either to all or sundry or
        to a specific group.  For example, some authors require written
        permission before a commercial disk vendor may copy their
        Shareware.

        You should find software that suits your needs and pocketbook,
        whether it's commercial or Shareware.  The Shareware system makes
        fitting your needs easier, because you can try before you buy.
        And because the overhead is low, prices are low also.  SHAREWARE
        HAS THE ULTIMATE MONEY-BACK GUARANTEE: IF YOU DON'T USE THE
        PRODUCT, YOU DON'T PAY FOR IT.  But if you do use it, you MUST
        pay for it.


                                                Double Directory  6

                                ================
                                  What Is ASP?
                                ================

        The Association of Shareware Professionals (ASP) is an industry
        association founded in 1987 to which authors and vendors of
        Shareware programs belong.  As a user of Shareware, you benefit
        from ASP activities.  ASP promotes broad distribution of
        Shareware so that ASP Shareware programs can continue to be
        reasonably priced and easily obtained.  ASP sets and maintains
        programming, marketing and support standards that members must
        follow; thus, you can be sure that ASP Shareware programs are of
        high quality, marketing is honest and support meets minimum
        standards.  For example, the evaluation copy of an ASP Shareware
        program may not be limited (crippled) in any way; members must
        respond to every registration; members must provide technical
        support for their products for at least 90 days from the date of
        registration.  Should an ASP member move or obtain a new
        telephone number, you can locate him or her through the ASP
        Executive Director, 545 Grover Road, Muskegon, MI 49442 USA,
        CompuServe 72050,1433, FAX 616-788-2765, Voice 616-788-5131.

        This program is produced by a member of the Association of
        Shareware Professionals (ASP).  ASP wants to make sure that the
        shareware principle works for you.  If you are unable to resolve
        a shareware-related problem with an ASP member by contacting the
        member directly, ASP may be able to help.  The ASP Ombudsman can
        help you resolve a dispute or problem with an ASP member, but
        does not provide technical support for members' products.  Please
        write to the ASP Ombudsman at 545 Grover Road, Muskegon, MI
        49442-9427 USA, FAX 616-788-2765 or send a CompuServe message via
        CompuServe Mail to ASP Ombudsman 70007,3536.

        You can obtain "The Shareware Compendium," a 768 page catalog of
        ASP Shareware from many bookstores and directly from the ASP
        offices.

                    ===========================================
                      Why Should I Register Double Directory?
                    ===========================================

        Double Directory is a copyrighted shareware product; it is not
        freeware or public domain.  You can try it before you buy it and
        you are encouraged to give copies to others (see "Warranty/
        License/Support" for conditions).  If you like it and use it, you
        should send the registration fee of $15.00 (U.S. dollars) to 100%
        Cotton Software, RR 1 Box 1622, Hop Bottom, PA 18824.  There is a
        registration form at the end of this manual and in REGISTER.DOC.

        When you register Double Directory, you will receive:
        1. the latest version of the program
        2. which does not have any request for registration screens and


                                                Double Directory  7

           which recognizes the /s skip switch (see Command-Line
           Parameters section);
        2. unlimited, life-time, free (not toll-free) telephone and mail
           support;
        3. notifications of updates;
        4. discounts on updates;
        5. a copy of our program, Clip and Save;
        6. your choice of one of our other shareware programs (see
           PRODUCTS.DOC for a description of the programs);
        7. and, of course, the appreciation of programmers who strive to
           produce inexpensive, quality, useful and entertaining
           software.

                          ============================
                            Warranty/License/Support
                          ============================

        User Groups, Computer Clubs, Disk Vendors and Distributors,
        Subscription Services, Disk-of-the-Month Clubs, etc. should refer
        to VENDOR.DOC for complete information relating to them.  BBS
        SYSOPs should refer to SYSOP.DOC for complete information
        relating to them.

        The author believes that Double Directory is able to do what this
        documentation says it can do.  Every good-faith effort has been
        made to remove "bugs" from this program and to make the user
        aware of its limitations.  However, it is mathematically
        impossible to prove a computer program correct.  Users of Double
        Directory must accept this disclaimer of warranty: DOUBLE
        DIRECTORY IS SUPPLIED AS IS.  THE AUTHOR DISCLAIMS ALL
        WARRANTIES, EXPRESSED OR IMPLIED, INCLUDING, WITHOUT LIMITATION,
        THE WARRANTIES OF MERCHANTABILITY AND OF FITNESS FOR ANY PURPOSE.
        THE AUTHOR CANNOT BE HELD LIABLE FOR ANY DAMAGES, INCLUDING ANY
        LOSS OF PROFIT, DATA OR OTHER SPECIAL, INCIDENTAL OR
        CONSEQUENTIAL DAMAGES OR SIMILAR CLAIMS ARISING OUT OF THE USE OF
        THIS PROGRAM.

        Double Directory is a copyrighted, shareware program and is
        provided at no charge to the user for evaluation.  You are
        granted permission to copy the Double Directory disk for your own
        (evaluation) use and for others to evaluate, only when the
        following conditions are met.  (1) The Double Directory package
        is defined as containing all the material listed in PACKING.LST.
        If any files listed in PACKING.LST (including PACKING.LST) are
        incomplete or missing, then the Double Directory package is
        incomplete and distribution is forbidden. (2) No file of the
        Double Directory package may be modified in any way.  (3) No
        compensation of any sort may be charged for the Double Directory
        package, except for a maximum of $5.00 (U.S. dollars) for the
        cost of the disk and shipping and handling. (4) The Double
        Directory package cannot be sold as part of another package,
        included in any commercial software package, rented or leased,


                                                Double Directory  8

        without written agreement from the author. (5)  You may not
        modify, decompile, disassemble, or otherwise reverse engineer
        Double Directory.  The essence of Shareware software is to
        provide personal computer users with quality software without
        high prices, and to provide incentive for programmers to continue
        to develop new products.  Your adherence to the above conditions
        makes this possible.

        You are granted a limited license to use this program for
        evaluation purposes for a period not to exceed sixty (60) days.
        If you find Double Directory useful and continue to use it after
        60 days, you must make a registration payment of $15.00 (U.S.
        dollars) to 100% Cotton Software, RR 1 Box 1622, Hop Bottom, PA
        18824.  International users should add $3 U.S. dollars.

        The registration fee will license one copy of Double Directory
        for use on any one computer at any one time.  You must treat this
        software just like a book.  That is, this software may be used by
        any number of people and may be freely moved from one computer
        location to another, so long as there is no possibility of it
        being used at one location while it's being used at another (just
        as a book cannot be read by two persons at the same time at two
        different locations).

        If more than one copy of Double Directory is used on more than
        one computer at the same time, each copy of Double Directory must
        be individually registered or a special license must be obtained.
        Low-cost site, multiple-copy, and school licenses are available.
        Write to 100% Cotton Software, RR 1 Box 1622, Hop Bottom, PA
        18824 or call 717-289-4019.


        Registered owners of Double Directory will receive free support
        for the lifetime of the product.  You can call (not toll-free)
        717-289-4019 or send a letter to the above address.

                           ==========================
                             Using Double Directory
                           ==========================

        When Double Directory is first run, it stops at the title screen,
        where you can change the paths or masks of each directory,
        continue with the default paths and masks or quit the program.
        The default paths are both set to the active drive and directory
        when Double Directory is run.  The default masks are "*.*".
        Paths and masks can be changed at this point or overridden via
        command-line parameters (see below).  It then reads and displays
        both directories.

        ------
          F1    Pressing F1 activates context-sensitive help.  For
        ------  example, if you are entering a path and press F1, you


                                                Double Directory  9

        will get help on entering a path, but if the tag menu is active
        when you press F1 you will get help about tagging.  See also
        "Help" in the TIPS section.

        --------------
          The Screen    A vertical line divides the screen into left and
        --------------  right directory windows (where the files are
        listed).  A horizontal line five lines from the bottom of the
        screen, separates the directory windows from the directory
        information area.

        Double Directory uses a single-line menu system at the top of the
        screen.  The last choice you make at any menu is remembered and
        offered as the default the next time you activate that menu,
        except in some cases such as offering "No" for Exit and "Yes" for
        Confirm.  The main menu is activated from within either directory
        window by pressing F10 or "/" (familiar to Lotus 1-2-3 users).
        Use the arrow keys to move the menu bar and press Enter to select
        an item.

        At the bottom of the screen is a help line that gives information
        about the menu items as the menu bar moves over them.  When you
        choose a menu item that invokes another menu, that menu replaces
        the current menu and a title is placed at the left of the menu
        line to remind you where you are in the menu system.  For
        example, if you press F10 from either directory window you will
        see:
          File  Directory  Options            Help
        If you then choose File, you will see:
          FILE: Delete Rename Copy View Move Tag Attributes DOS Exit
        If you then choose Tag, you will see:
          FILE/TAG:  Tag  Untag  Toggle

        In the left and right directory windows, Double Directory
        displays the name, extension, size, and date of each entry in the
        directory.  It also displays either the entry's time or its
        attributes depending upon the setting of Options/Dir/Time.

        Double Directory displays all subdirectories in the path.
        "<parent>" or "<subdir>" is substituted for the subdirectory's
        size.  The parent directory (next higher level) is shown as "..".
        The volume name (if there is one) is shown as "<vol id>".

        All valid drives (root directories) are displayed as "a:\", "c:\"
        and so on with "<drive>" in place of their sizes.  The drive of
        the current directory is displayed (making it easy to move up to
        the root directory).

        In the directory information area at the bottom of the screen are
        displayed the complete path of each directory, the number of free
        bytes on that disk and the number of files (not subdirectories,
        volume names and drive entries) in the directory.


                                                Double Directory  10


        ----------------------------
          Moving Around the Screen    Use Up Arrow, Down Arrow, Home,
        ----------------------------  End, Page Up and Page Down to move
        the cursor bar forward and backward through a directory.  When
        there are more entries in a directory than will fit on screen,
        the listing will scroll up or down when the cursor bar reaches
        the top or bottom of the window.

        Use Left Arrow, Right Arrow, F6, Tab or Shift-Tab to move from
        one directory window to the other (activate it).  When the left
        directory window is active, a right arrow character is displayed
        on the horizontal divider line and when the right directory
        window is active, a left arrow character is displayed.  In
        addition to indicating which window is active, the character
        indicates the direction of the copy and move commands (to the
        left or right); the arrow indicates the source directory and
        points to the destination directory.  The cursor bar in the
        active directory window is a different color from the cursor bar
        in the inactive window.  Also, the active directory window is
        framed in a different color.  Thus, there are three visual clues
        as to which is the active directory window.

        If you press Scroll Lock, an "S" will appear (or disappear) at
        the intersection of the vertical and horizontal divider lines.
        When Scroll Lock is on, you can scroll through both directories
        simultaneously.  The cursor bars in both directories will be the
        active color (see "Colors" below).

        You can also use the WordStar keys for cursor movement and text
        entry (see keystroke chart at end of manual).

                             ======================
                               Executing Commands
                             ======================

        ----------
          F10, /    Pressing F10 or "/" activates Double Directory's menu
        ----------  system by which you can execute its various
        functions.  For example, to change the sort criteria to "sort by
        descending size" from either of the directory windows, you would
        press F10 and move the menu bar to "Directory" and press Enter.
        Then move the menu bar to "Sort" and press Enter.  Next move the
        menu bar to "Size" and press Enter and finally move to
        "Descending" and press Enter.  You could also use the menu hot
        keys: press F10, I, S, S, D.

        Most of Double Directory's functions have hot keys which make it
        easier to activate them.  For example, when in either of the
        directory windows you can press "S" and the Sort menu will be
        activated or "B" and the Attributes menu will be activated.


                                                Double Directory  11

        -------
          Esc    Pressing Esc always moves you backward one step.  In the
        -------  example above, pressing Esc when you have reached the
        menu that offers Ascending or Descending will take you back to
        the Sort menu and pressing Esc again will take you back to the
        Directory menu.  Or if you have tagged several files to rename,
        and want to stop part way through the list, just press Esc.

        When printing a file, Double Directory checks whether you have
        pressed Esc (to cancel printing) at every line.  When you press
        Esc to cancel while copying, deleting, moving, etc., the cancel
        takes effect before the execution of the function upon the next
        file.

        -------------
          Shift-F10    Pressing Shift-F10 moves you backward all the way.
        -------------  It is like pressing Esc several times.  In the
        example above, pressing Shift-F10 at the Ascending/Descending
        menu will cancel all menus and place you back into the active
        directory window.  Or, if you have tagged a number of files for
        viewing and decide part way through the list that you don't want
        to view any more, press Shift-F10 to cancel viewing (pressing Esc
        will cancel viewing of the current file and proceed on to the
        next).

        ---------
          Enter    Press Enter while the cursor bar is on a directory or
        ---------  drive entry to change the path for that directory
        window.  The new directory path will be read and displayed.  For
        example, let's say the path in the active directory is
        C:\LETTERS\.  If you place the cursor bar on the subdirectory
        entry "MARCH" and press Enter, the new path will be
        C:\LETTERS\MARCH.  If you now place the cursor bar on the entry
        ".." (parent directory) and press Enter, the new path will be
        C:\LETTERS\.  If you now place the cursor on "A:\" and press
        Enter, the new path will be A:\.  Using the direction keys and
        Enter, you can easily and quickly choose and display directories
        of different disks and move up and down through the subdirectory
        structure of a disk.

        Pressing Enter while the cursor bar is on a filename or volume
        name does nothing.

        -----------------
          Tagging Files    A file must be tagged before it can be
        -----------------  acted upon (deleted, copied, etc.).  To tag a
        file, place the cursor bar on the directory entry of the file you
        want to tag and press Ins (or File/Tag from the menu).  The tag
        character will appear to the left of the filename.  To untag a
        file, press Del (or File/Untag from the menu); the tag character
        will disappear.  Pressing the spacebar or choosing File/Toggle
        tags an untagged file or untags a tagged file.


                                                Double Directory  12


        F7 (or Directory/Tag) tags all of the files in the active
        directory and F8 (or Directory/Untag) untags all of the files in
        the active directory.  Shift-F7 and Shift-F8 toggle all the tags
        in a directory.  You can tag files in either or both directories.

        Functions that operate upon files (copy, delete, etc.) work with
        the tagged files (only) in the active directory.  Functions that
        operate directly upon directories (make, remove) work on the
        currently highlighted subdirectory name in the active directory.
        That is, a directory is not tagged before it is operated on.  You
        simply place the cursor bar on the directory name and then choose
        a function like Remove (therefore, only one subdirectory at a
        time can be acted upon).  Other functions like Sort or Compare
        work upon the entire active directory; nothing needs to be tagged
        or highlighted.

        -----------------
          Entering Text    Whenever you select a function that requires
        -----------------  you to enter text, the editing keys are
        activated.  For example, when you choose Mask, Path or Rename,
        the current filename, mask or path is displayed at the top of the
        screen and the cursor is placed at the end of it.  You can press
        Backspace to delete characters and Del to delete the entire
        string of characters.  As you type, Double Directory checks that
        you enter valid mask, file or path characters, that you do not
        enter "." more than once, and that you do not exceed the legal
        length.

        However, if you are entering command-line parameters for Shell
        and run or Clear and run, only the length is checked; every
        character you type is accepted.

                             =======================
                               Functions Reference
                             =======================

        In the following sections each function is discussed.  The hot
        keys and function keys are shown at the right.

        Pressing F10 or "/" activates the main menu which has entries for
        File, Directory, Options and Help.

        -------------------
          MAIN | FILE | L    The file menu has entries for deleting,
        -------------------  renaming, copying, viewing, moving and
        tagging files; changing file attributes; shelling to DOS/running
        programs; and exiting Double Directory.

        You may delete, rename, copy, view, move, tag and change the file
        attributes of more than one file at a time.  You will be asked to
        confirm the action for each file if Options/Confirm is set to


                                                Double Directory  13

        Yes.  Delete ALWAYS asks if you want to confirm each deletion.

        ------------------------
          MAIN | DIRECTORY | I    The directory menu has entries for
        ------------------------  comparing, sorting, rereading, making
        and removing directories; changing directory paths and masks;
        tagging/untagging and toggling the tags of all files in a
        directory; and displaying information.

        ----------------------
          MAIN | OPTIONS | T    The options menu has entries for
        ----------------------  displaying 25 or 43/50 rows; toggling
        sound on/off; toggling confirm action on/off; choosing the
        directory options, the colors, and the view options menus;
        setting the path to dbldir.exe and dbldir.hlp; and saving the
        options to disk.

        -------------------
          MAIN | HELP | H    Pressing "H" gives you access to all of the
        -------------------  help text.  When the help window opens, use
        the Page Up and Page Down keys to page through the text.

                               ==================
                                 File Functions
                               ==================

        ---------------------
          FILE | DELETE | D    Double Directory first asks if it should
        ---------------------  confirm the deletion of the tagged files
        one-at-a-time (the safest approach) or delete them nonstop.  If
        you choose individual deletion, it will show each filename and
        request confirmation.  If you choose Yes, the file will be
        deleted.  If you choose No, that file will be skipped (not
        deleted) and the next filename (if more than one file is tagged)
        will be presented.

        You are always required to choose a deletion mode (one-at-a-time
        or nonstop) because if you inadvertently delete a file, you will
        have to find your backup disk or use another Shareware utility
        program to undelete the file.

        ---------------------
          FILE | RENAME | N    If Options/Confirm is set to Yes, you
        ---------------------  will be asked to confirm that you want to
        rename each tagged file in order.  If you answer No, then that
        file is skipped.  If you answer Yes, then the tagged filename is
        displayed at the top of the screen.  You can edit it or enter a
        new filename (see Editing above).  If a file with the same name
        already exists, an error message will be displayed and that file
        will be skipped.


                                                Double Directory  14

        -------------------
          FILE | COPY | C    If Options/Confirm is set to Yes, you will
        -------------------  be asked to confirm that you want to copy
        each tagged file in order.  If you answer No, then that file is
        skipped.  If the source file already exists in the destination
        directory and Options/Confirm is set to Yes, you will be asked if
        the file in the destination directory should be replaced with the
        source copy.  If Options/Confirm is set to No and the file
        already exists in the destination directory, the source copy will
        replace the file without requesting confirmation (so be careful).

        Double Directory does not check whether there is enough free
        space to copy the files because that would depend upon whether
        you want to replace existing file or not.  If there isn't enough
        room, it will display a "Disk Full" error message and delete the
        partially copied file in the destination directory.  If
        Options/Confirm is set to No and the destination disk becomes
        full, then the copy of the file on the destination file will be
        deleted: that is, Double Directory deletes the file on the
        destination disk without confirmation, starts copying the source
        file, finds the disk full, issues an error message and deletes
        the partially copied file on the destination disk.  The source
        file is still there.

        If several files are tagged and the disk becomes full, after
        issuing the error message, Double Directory will attempt to copy
        the next tagged file (which may be smaller and may fit).  You can
        determine if there is enough room to copy the tagged files by
        pressing F2; see Directory/Info below.  Of course, you can press
        Esc or Shift-F10 to cancel copying.

        Either directory can be the source or destination for the Copy
        function.  Whichever directory window the cursor bar is in and is
        framed in double lines is the active directory and the source
        directory; the other is the inactive directory and the
        destination.  The arrow character on the horizontal dividing line
        indicates the active (source) directory and points to the
        destination directory.

        -------------------
          FILE | VIEW | W    If Options/Confirm is set to Yes, you will
        -------------------  be asked to confirm that you want to view
        each tagged file in order.  If you do, a view window is opened
        and 18 lines from the file are displayed.  Use the direction keys
        to scroll through the file and press Esc or Shift-F10 to stop
        viewing.  While viewing a file, you may see the messages
        "Reading" or "Parsing" displayed at the top of the screen.  They
        are not error messages; they are meant to keep you informed about
        what is happening if you are using a slow computer system.  While
        viewing a file, you can press "V" to activate the Options/View
        menu (see below) which enables you to print the file, turn line
        wrap on or off, and so on.


                                                Double Directory  15


        View file can handle any size file because it reads and parses
        only part of the file at a time.  It is designed for browsing a
        file for its contents.  If you need more power (you need to see a
        file in exactly its original format or you need to search for
        specific items in a file), you should obtain a more specialized
        Shareware file-viewing utility.

        -------------------
          FILE | MOVE | V    If Options/Confirm is set to Yes, you will
        -------------------  be asked to confirm that you want to move
        each tagged file in order.  There are two move modes: (1) if the
        source and destination paths are on different drives, move copies
        and then deletes a file; (2) if they are on the same drive but in
        different subdirectories, it simply moves the file's directory
        entry from the source path to the destination path.  If the paths
        are identical, Double Directory will issue an error message.

        If you are moving files between different disks, Double Directory
        copies the files from the source to the destination path and then
        deletes them from the source path.  If you press Esc to cancel,
        the files copied up to when you pressed Esc will remain tagged
        since they were copied but not deleted.

        If Options/Confirm is set to Yes, you will be prompted to confirm
        the move of each file, but not prompted to confirm the deletion
        of each file even if the source and destination paths are on
        different disks since the files have already been copied.

        -------------------------
          FILE | TAG | Ins, Del    See "Tagging" above.
        -------------------------

        -------------------------
          FILE | ATTRIBUTES | B    DOS assigns an attribute bit to
        -------------------------  each directory entry.  READ ONLY files
        can't be written to or deleted by DOS.  HIDDEN files are
        invisible to most DOS operations (including dir).  SYSTEM files
        are also invisible to most DOS operations (they are a carry-over
        from CP/M days).  The ARCHIVE bit indicates that a file has been
        modified but not backed up.  The volume and subdirectory
        attributes indicate that the entry is a volume name or a
        subdirectory; Double Directory does not enable you to change the
        volume or subdirectory attributes.

        If Options/Confirm is set to Yes, you will be asked to confirm
        that you want to change the attributes of each tagged file in
        order.  As you toggle an attribute on or off, an "A", "H", "R" or
        "S" will appear or disappear after the file's name.  When you
        have set the attributes as you want, choose Done and the
        attributes will be written to disk.


                                                Double Directory  16

        Unlike DOS, Double Directory can view, rename, copy, etc. files
        with hidden, system and read-only attributes.  This is one reason
        for using it instead of DOS.  However, because it can, for
        example, delete a hidden or read-only file you should be very
        careful.  Also, if you set a file's Hidden attribute, it will not
        be visible to the DOS dir command.

        When Double Directory copies a hidden, system or read-only file,
        the copy will be hidden, system or read-only; that is, the file
        attributes are preserved.  All copied files have the archive bit
        set.

        If Options/Dir/Time is set to No, a file's attributes are
        displayed in the directory windows; otherwise, its time is shown.

             ******************
             * Technical Note *  A false attribute is assigned to drives
             ******************  in a directory file list (hex F0).  You
             cannot change this attribute.  The attributes are used for a
             number of things, including determining whether a filename
             can be tagged or if it is a drive or subdirectory.  This
             false attribute will cause no problems with DOS.  However,
             we cannot state with certainty that it will not cause
             problems with all networks.  There are many types of
             networks and they are constantly being revised.

             This version of Double Directory is not network aware; that
             is, it does not lock or unlock a file or check its status
             when it accesses a file.

        ------------------
          FILE | DOS | O    There are four choices on the DOS menu.
        ------------------

          ----------------------
            FILE | DOS | SHELL    Shell enables you to temporarily exit
          ----------------------  Double Directory to the command line
          from which you can issue DOS commands, such as dir, cd, mkdir,
          and so on, or run another program (if there is enough memory).
          The screen will clear and you will see the DOS prompt.  When
          you are ready to return to Double Directory, type "exit" and
          press Enter (at the DOS prompt).  When you shell to DOS,
          another copy of command.com is loaded; if it can't be found,
          you will be immediately returned to Double Directory.

          The directories aren't reread after you return from DOS.  So,
          if you make changes by making or removing directories, adding
          files, etc., you should reread the directories by pressing F9,
          switching to the other directory window and pressing F9 again.


                                                Double Directory  17

          ----------------------------
            FILE | DOS | SHELL & RUN    Shell and run enables you to
          ----------------------------  temporarily exit to DOS and run
          the first tagged file in the active directory and then return
          to Double Directory (which remains in memory).  The program
          must have an .exe, .com or .bat extension.  Before the program
          is run, you are given the opportunity to enter a command-line
          that will be passed to the program when it runs.  The command-
          line string can be up to 64 characters long and all characters
          are valid.  If you do not need to pass a command-line to the
          program, do not type anything; just press Enter.  You will be
          returned to Double Directory immediately if command.com cannot
          be located or if there is not enough memory to run the
          program.

          Renaming or deleting the file dbldir.hlp so that it cannot be
          found when Double Directory is run, makes about 11K more
          memory available to Shell and run.

          ----------------------------
            FILE | DOS | CLEAR & RUN    Clear and run temporarily
          ----------------------------  removes Double Directory from
          memory, runs the first tagged file and then returns to Double
          Directory.  As with Shell and run, the program must be have an
          .exe, .com or .bat extension and you are given the opportunity
          to enter a command-line string (see above).  Since Double
          Directory is removed from memory, there is much more memory
          available to the program you want to run.  Clear and run
          enables you to use Double Directory as a shell or menu
          program.  Be sure to read Options/Path below.  See also "Using
          Double Directory as a Shell" in the TIPS section below.

          The combined length of the command line and the path to the
          program and the name of the program cannot exceed 124
          characters.  Therefore, if you attempt to Clear and run a
          program that lies at the maximum depth in the subdirectory
          structure of your disk (79 characters including the program
          name) and you pass more than 45 characters of parameters to
          the program, the total length could exceed 124 characters, in
          which case Double Directory might not be able to find its way
          back so it can rerun itself after the program has finished.

             ******************
             * Technical Note *  When you choose Clear and run, Double
             ******************  Directory creates a temporary batch file
             named $dbldir$.bat in the directory of the program that is
             being run.  You should not rename or delete this file while
             you are shelled out of Double Directory (which will delete
             it when you return).  This file is NOT hidden so if your
             computer crashes due to a power glitch or if you shut down
             your computer before returning to Double Directory you will
             be able to find $dbldir$.bat and delete it if you want.


                                                Double Directory  18

             Many programs create temporary hidden files and if anything
             goes wrong you may not know that a hidden file is taking up
             space on your disk.

          ---------------------------
            FILE | DOS | EXIT & RUN    Exit and run enables you to quit
          ---------------------------  Double Directory and run the
          first tagged file.  As with Shell and run, the program must
          have an .exe, .com or .bat extension and you are given the
          opportunity to enter a command-line string.  Also, you are
          prompted to confirm that you want to Exit and run.

        -----------------------
          FILE | EXIT | X, F3    You are always prompted to confirm
        -----------------------  that you want to exit.  When you return
        to DOS, you will be in the same directory as when you started
        Double Directory.

                             =======================
                               Directory Functions
                             =======================

        ------------------------
          DIRECTORY | PATH | P    Double Directory uses a left and right
        ------------------------  path (and mask) to read and display the
        directories in the left and right directory windows.  Each
        directory window can have a different path or the same path.  The
        path may be as simple as a drive designation (A:\) or a
        combination of a drive and subdirectories (C:\LETTERS\PERSONAL\).
        Double Directory adds the colon (:) and trailing backslash (\) if
        it is omitted.  Thus, if you simply want to change drives, press
        "P" for path, "Del" to delete the path, the new drive letter, and
        Enter.  Or you could type "cgames" and Double Directory would
        change this to "c:\games\".  Double Directory checks the length
        of the path you enter and accepts only valid path characters (see
        your DOS manual for more information).

        When you first run the program, both the left and right paths are
        set to the path from which you started Double Directory.  You are
        given an opportunity at the title screen to change the paths and
        masks.

        You rarely need to press "P" to change the path (except at the
        title screen), because it is easier to point and shoot to add or
        delete subdirectories to/from the path.  When Double Directory
        displays a directory, it shows subdirectories as well as
        filenames.  Like DOS it shows the parent directory as "..".  It
        shows "<subdir>" and "<parent>" in place of the file size.  To
        add to or delete from the path, place the cursor bar on the
        subdirectory name and press Enter.  The name will be appended or
        deleted and the new directory will be read and displayed.  This
        makes Double Directory a very useful tool for navigating a hard


                                                Double Directory  19

        disk (looking for a file, for example).  Double Directory does
        not show "." (the current directory).

        A path's length cannot exceed 67 characters and must include a
        drive letter and zero or more subdirectories.

             ******************
             * Technical Note *  Some versions of DOS allow you to create
             ******************  paths deeper than a 67-character path
             allows.  There is nothing we can do about this.  So if you
             are using one of these aberrant versions of DOS, you may
             work your way down through several subdirectories and
             eventually hit a dead end (there will be no parent directory
             ".." displayed).  At this point the path will exceed 67
             characters and be truncated and make no sense to Double
             Directory.  If this happens, just press "P" and enter a new
             path or place the cursor bar on a drive entry and press
             Enter to jump upward.

        ------------------------
          DIRECTORY | MASK | M    The mask is used when Double Directory
        ------------------------  reads the directory from disk; it acts
        as a filter for including/excluding entries.  A mask is composed
        of a name of up to 8 characters, a period, and an extension of up
        to 3 characters.  It may include the wildcard characters "*" and
        "?".  "*" means include any number of characters and "?" means
        include any one character.  The default mask is "*.*"; all files
        (characters) are included.  You would change the mask if you want
        to display only a select group of directory entries.  For
        example, if the mask is "*.BAS" then only files with the "BAS"
        extension are included.  Each directory window can have a
        different mask.  Double Directory checks the length of the mask
        you enter and accepts only valid filename (mask) characters (see
        your DOS manual for more information).

        ---------------------------
          DIRECTORY | COMPARE | M    All files in the left and right
        ---------------------------  directories are compared according
        to the criteria you select.  Each file that does not have a match
        in the other directory is tagged.  The criteria are additive; for
        example, if you choose DATE, files must match by name AND size
        AND date.

          ------------------------------
            DIRECTORY | COMPARE | NAME    All files in the two
          ------------------------------  directories are compared by
          their 8-character names and 3-character extensions.  Use this
          to determine whether files in one path are in another.


                                                Double Directory  20

          ------------------------------
            DIRECTORY | COMPARE | SIZE    All files in the two
          ------------------------------  directories are compared by
          name and then by size (in bytes).

          ------------------------------
            DIRECTORY | COMPARE | DATE    All files in the two
          ------------------------------  directories are compared by
          name, then by size and then by date.

          ------------------------------
            DIRECTORY | COMPARE | TIME    All files in the two
          ------------------------------  directories are compared by
          name, then by size, then by date and then by time.  Use this
          to determine whether the latest versions of files in one path
          are in another.

        ------------------------
          DIRECTORY | SORT | S    Directories can be sorted by name,
        ------------------------  extension, size, date or time in
        ascending or descending order.  You can also display a directory
        in unsorted order (as with the DOS dir command).  All entries in
        a directory are sorted: files, subdirectories and drives.
        Ascending order is "A" to "Z" and "0" to "9".  Each directory can
        have different sort criteria.  Sorting only affects the way the
        directory entries are displayed; nothing on the disk is changed.

          ---------------------------
            DIRECTORY | SORT | NAME    All entries in the directory are
          ---------------------------  sorted by their 8-character
          names.

          --------------------------------
            DIRECTORY | SORT | EXTENSION    All entries in the directory
          --------------------------------  are sorted by their 3-
          character extensions.  Since drives have no extensions, they
          will appear first or last in the directory listing depending
          upon whether the sort order is ascending or descending.

          ---------------------------
            DIRECTORY | SORT | SIZE    All entries in the directory are
          ---------------------------  sorted by their sizes.  Since
          subdirectories and drives have no sizes, they appear first or
          last in the directory listing depending upon whether the sort
          order is ascending or descending.

          ---------------------------
            DIRECTORY | SORT | DATE    All entries in the directory are
          ---------------------------  sorted by their dates.  Since
          drives have no dates, they appear first or last in the
          directory listing depending upon whether the sort order is
          ascending or descending.


                                                Double Directory  21


          ---------------------------
            DIRECTORY | SORT | TIME    All entries in the directory are
          ---------------------------  sorted by their times.  Since
          drives have no times, they appear first or last in the
          directory listing depending upon whether the sort order is
          ascending or descending.

          ------------------------------
            DIRECTORY | SORT | NO SORT    Unsorted first displays the
          ------------------------------  drives and then the files and
          directories unsorted.

        ------------------------------
          DIRECTORY | REREAD | E, F9    Reread causes Double Directory
        ------------------------------  to read the directory of the path
        of the active directory window.  It is useful to quickly look at
        the directories of several floppy disks.  Put a disk in the drive
        and press F9 to see the directory listing.  Put another disk in
        the drive and press F9 again.  Repeat until you find the disk you
        want.

        ------------------------------------------------
          DIRECTORY | TAG | F7, F8, Shift-F7, Shift-F8    F7 tags all of
        ------------------------------------------------  the filenames
        (not subdirectories) in the active directory and F8 untags all of
        the filenames.  See "Tagging" above.  Shift-F7 and Shift-F8
        toggle the tags of all filenames in the active directory: all
        tagged filenames are untagged and all untagged filenames are
        tagged.

        ------------------------
          DIRECTORY | MAKE | K    Make allows you to create a new
        ------------------------  subdirectory at the end of the path of
        the active directory window (like the DOS mkdir command).  Place
        the cursor bar in the desired directory window before selecting
        Make.  If Options/Confirm is set to Yes, you will be asked to
        confirm that you want to create a new subdirectory.  Subdirectory
        names, like filenames, may be comprised of an 8-character name, a
        period, and a 3-character extension.  If a file or subdirectory
        with the same name already exists, an error message will be
        displayed.

        --------------------------
          DIRECTORY | REMOVE | R    Remove allows you to remove an empty
        --------------------------  subdirectory (like the DOS rmdir
        command).  Place the cursor bar on the directory name you wish to
        remove before selecting Remove.  If Options/Confirm is set to
        Yes, you will be prompted to confirm that you want to remove the
        subdirectory.  If the directory is empty, it will be removed; if
        it still contains one or more files or subdirectory entries, an
        error message will be displayed.  Remove only requests


                                                Double Directory  22

        confirmation if Options/Confirm is set to Yes, since it will only
        remove an empty directory (which is easily recreated).

        ----------------------------
          DIRECTORY | INFO | F, F2    The information screen displays
        ----------------------------  several pieces of information: the
        current date and time; the version of DOS being used; the total
        number and combined size of the tagged files; the name (in
        brackets []) of the file to which Options will be saved (usually
        dbldir.exe); the total number of bytes, the number of free bytes
        and the cluster size of each disk; and the amount of free memory.

        The combined size of the tagged files is useful for determining
        how much space is necessary on the destination disk to copy the
        tagged files.  Bytes "free" and bytes "tagged" can be used to
        determine if there is enough free disk space to copy files.
        However, disks can have different cluster sizes -- the smallest
        disk space that can be allocated.  Thus, if the cluster size is
        1024, a 65 byte file requires at least 1024 bytes.

        The amount of free memory shows the approximate amount of memory
        available to Shell and run.

        Of course, the current paths and masks for the left and right
        directory windows are shown at the bottom of the screen.

                               =====================
                                 Options Functions
                               =====================

        -------------------
          OPTIONS | SOUND    Double Directory "beeps" only to call your
        -------------------  attention to something such as an error
        condition.  You can toggle the sound on or off.

        -------------------------
          OPTIONS | CONFIRM | F    When confirm is set to Yes, you are
        -------------------------  prompted to confirm that you want to
        execute some functions.  For example, if Confirm is set to Yes
        and several files are tagged, when you press "C" to copy the
        files, you will be asked to confirm copying of each file in its
        turn.  Setting confirm to Yes is safest, although it does take a
        bit more time to answer each confirmation request; it prevents
        inadvertently deleting files or replacing files with copies.
        Confirm affects both directories; either it is on or off for
        both.

        ------------------
          OPTIONS | ROWS    Press "2" to display 25 rows and "4" to
        ------------------  display 43 rows if you are using an EGA
        display adapter or 50 rows if you are using a VGA.  Double
        Directory will show 19 entries in each directory in 25-row mode,


                                                Double Directory  23

        37 entries in 43-row mode, and 44 entries in 50-row mode.

        -----------------------
          OPTIONS | DIRECTORY    Via this menu you can toggle on/off the
        -----------------------  display of a file's time and adjust the
        maximum number of directory entries.

          ------------------------------
            OPTIONS | DIRECTORY | TIME    When On, a file's time is
          ------------------------------  displayed; when Off, its
          attributes are displayed (see File/Attributes above).

          ------------------------------
            OPTIONS | DIRECTORY | SIZE    Size (the maximum number of
          ------------------------------  directory entries) --
          filenames, subdirectories, drives -- can range from 28 to 800.
          The lower the number, the more room there is for DOS/Shell and
          run.

          When shipped, Double Directory is set to handle 150 entries in
          each directory window.  It automatically determines how many
          entries there are in a directory and manages memory allocation
          automatically; it will increase Size appropriately.
          Occasionally you will briefly see the message "Adjusting
          memory" at the bottom of the screen and both directory windows
          will clear and then refill.  The message is displayed simply
          to keep you informed; it is not an error message.  However, if
          there is not enough memory for Double Directory to read all of
          the entries from the disk, you will see error message -4 (see
          below).  This can happen if your computer does not have enough
          memory or if you have filled memory with TSRs, drivers and
          other programs.  In this case Double Directory will read and
          display as many entries as there is room for.  You should quit
          and rerun Double Directory with more memory available (remove
          TSRs, etc.) since you will not see the complete directory.  Of
          course, if the directory has more than 800 entries, Double
          Directory will not be able to read all of them because this is
          the absolute maximum it can handle.

          The only reason you might want to manipulate Options/
          Directory/Size would be to decrease its size (Double Directory
          does not adjust the maximum directory size downward -- only
          upward when necessary).  The smaller Size is, the more memory
          that is available to DOS/Shell and run.

             ******************
             * Technical Note *  The directory entries are held in a
             ******************  two-dimensional array: FileList
             (2,MaxDirSize).  If MaxDirSize has to be increased, the
             array is redimensioned, so both dimensions are cleared and
             both directories are reread.


                                                Double Directory  24

             With other file utility programs which handle only one
             directory, memory management is totally hidden from you.
             Because Double Directory handles two directories (and you
             can see BOTH) and must reread both if either exceeds
             MaxDirSize, you see something happening.

        ----------------------
          OPTIONS | VIEW | W    This menu can be accessed as any other
        ----------------------  menu is accessed AND while viewing a
        file.  There are five options that determine how a file is
        displayed on screen or printed and one option for printing files.

        Generally, you should have Wrap set to No, EOL Char set to LF,
        Show CR/LF set to No, High bit set to No and Show CTRL chars set
        to No.

        If you change EOL Char and/or Wrap while viewing a file, the
        display will clear and viewing will start again at the beginning
        of the file.

          -----------------------------
            OPTIONS | VIEW | HIGH BIT    If set to Yes, High Bit strips
          -----------------------------  the high bit off each character
          displayed: characters with ASCII values of 127 or higher are
          converted to characters with ASCII values less than 128.  For
          example, the character "-" is converted to "A".  This is
          useful when viewing files created by WordStar which sets the
          high bit of some characters for formatting purposes.  However,
          if the file you are viewing uses the box drawing characters
          (as this file does) or the international characters and you
          set High bit to Yes, the file may not make much sense as you
          view it.

          ------------------------------------
            OPTIONS | VIEW | SHOW CTRL CHARS    If set to NO, characters
          ------------------------------------  with ASCII values below
          32 (control characters) are replaced by the space character.
          This includes the tab character.  Control characters are often
          used for formatting text display and printing; they include
          line feed, carriage return, horizontal and vertical tab, form
          feed, escape, backspace, bell, and others.  If not filtered
          out, most printers will interpret them as control codes and
          messy printouts will result.  Double Directory places
          characters directly into display memory when you are viewing
          (not printing) a file so control characters have no effect on
          the screen display.

          -------------------------------
            OPTIONS | VIEW | SHOW CR/LF    If set to No, carriage
          -------------------------------  returns (ASCII 13) and line
          feeds (ASCII 10) are not displayed; this makes the text easier
          to read.  Generally, set this to No, unless you have a reason


                                                Double Directory  25

          to see exactly where lines and paragraphs end.

          -----------------------------
            OPTIONS | VIEW | EOL CHAR    Different programs use
          -----------------------------  different characters to signal
          end of line and end of paragraph.  DOS uses a carriage return
          and line feed pair to indicate both.  Word Perfect uses a
          carriage return to indicate line end (soft) and a line feed
          for paragraph end (hard).  WordStar uses a carriage return
          with the high bit set and a line feed to indicate end of line
          (soft) and a carriage return and line feed pair to indicate
          paragraph end (hard).  Generally, you should set EOL Char to
          CR, unless you are viewing a Word Perfect file.

          -------------------------
            OPTIONS | VIEW | WRAP    Use this option to turn line wrap
          -------------------------  on/off and to set the column at
          which lines are wrapped or truncated.

             ----------------------------------
               OPTIONS | VIEW | WRAP | YES/NO    If Yes, then lines are
             ----------------------------------  wrapped at Column;
             otherwise, lines are truncated at Column.

             ----------------------------------
               OPTIONS | VIEW | WRAP | COLUMN    This is the column at
             ----------------------------------  which lines should be
             wrapped or truncated.  It may range from 1 to 999.
             Generally, leave this set to 80 (the width of the screen).
             However it is useful to change this when printing a file.
             You can set your printer's left margin (or offset the paper
             in the printer so as to make a left margin) and set Wrap to
             Yes at column 65 (or so) to get left and right margins.  Or
             if your printer has a wide carriage and is able to print
             more than 80 columns or if you use your printer's compressed
             character set, you can set Column to 132 or larger and get
             more text on a page.

          When Wrap is set to Yes, you can view entire lines even if
          they are longer than the screen is wide (80 characters).
          However, (1) the original formatting will be disrupted; (2)
          when you scroll backward, the lines may wrap differently from
          when you scroll forward (especially if the text has been
          formatted with a word processing program and contains hard
          carriage returns), but the contents will be the same; (3) only
          long lines are wrapped, so the rest of the formatting will be
          the same.  In other words, if you set Wrap to Yes, you are
          interested in seeing all of the contents of the file and you
          do not really care about the format of the file.

          With this version of Double Directory, the maximum width of a
          line on screen is 80 characters, even if the display adapter


                                                Double Directory  26

          is capable of displaying more columns.

          Examples, using a line of 100 characters from a file:

          1. If Wrap is set to Yes and Column is set to 76, then 76
          characters will be displayed on one line and 24 on the next.

          2. If Wrap is set to Yes and Column is set to 86, then 80
          characters will be displayed on one line, 6 characters will
          not be displayed and 14 will be displayed on the next line.

          3. If Wrap is set to No and Column is set to 76, then 76
          characters will be displayed on one line and 24 will not be
          displayed.

          4. If Wrap is set to No and Column is set to 86, then 80
          characters will be displayed on one line, 14 will not be
          displayed.

          --------------------------
            OPTIONS | VIEW | PRINT    This option is active only when
          --------------------------  you are viewing a file.  Show CTRL
          chars and Show CR/LF are temporarily set to No during
          printing.  You can still set High Bit, EOL char and Wrap the
          way you want.

             ---------------------------------
               OPTIONS | VIEW | PRINT | PART    Choose this to print the
             ---------------------------------  part of the file visible
             in the view window.

             -----------------------------------
               OPTIONS | VIEW | PRINT | ENTIRE    Choose this to print
             -----------------------------------  the entire file.

             Double Directory currently supports only LPT1 as a printer
             port.  See the "mode" command in your DOS manual for
             information about redirecting printer output.

             You can cancel or pause printing by pressing Esc.  If you
             answer Yes to the "Cancel printing?" prompt, printing will
             stop.  Double Directory looks for the Esc key at the end of
             each line it prints.

        -------------------
          OPTIONS | COLOR    You can choose the foreground and background
        -------------------  colors of all display items.  After you have
        selected the item whose color you want to change, a color window
        will open displaying all 128 possible color combinations in 8
        rows (background colors) of 16 columns (foreground colors).  Use
        the direction keys to move the blinking smiley-face cursor to the
        color you want and press Enter.  You can press "B" instead of


                                                Double Directory  27

        Enter if you want the color to blink (maybe for the Tag
        character).  The color names and some sample text appear at the
        bottom of the color window.  Color changes take effect
        immediately.  If you have a monochrome display adapter, the color
        combinations yield: dim white on black; bright white on black;
        black on white (inverse); dim underlined; and bright underlined.

          --------------------------
            OPTIONS | COLOR | LEFT    This is the color of the entries
          --------------------------  in the left directory window.  For
          best results, it should be different from the right directory
          window color.

          ---------------------------
            OPTIONS | COLOR | RIGHT    This is the color of the entries
          ---------------------------  in the right directory window.
          For best results, it should be different from the left
          directory window color.

          --------------------------
            OPTIONS | COLOR | HELP    This is the color of the help text
          --------------------------  that appears on the bottom line of
          the screen and in the help window when you press "H" or F1.
          It is also the color used when viewing a file.  For best
          results, it should be a color combination that makes reading
          easy.

          --------------------------
            OPTIONS | COLOR | MENU    This is the color of all menu
          --------------------------  items that are not highlighted by
          the menu cursor bar.

          --------------------------
            OPTIONS | COLOR | DBAR    This is the color of the cursor
          --------------------------  bar in the active directory window
          (both windows if Scroll is On).  For best results, it should
          be bright and easy to distinguish from the other directory
          entries.

          --------------------------
            OPTIONS | COLOR | IBAR    This is the color of the cursor
          --------------------------  bar in the inactive directory
          window.  For best results it should be dimmer than the DBAR
          color but easily distinguished from the other directory
          entries.

          --------------------------
            OPTIONS | COLOR | MBAR    This is the color of the menu
          --------------------------  cursor bar.  For best results, it
          should be easily distinguished from the MENU color.


                                                Double Directory  28

          ----------------------------
            OPTIONS | COLOR | ALINES    This is the color of the double
          ----------------------------  horizontal and vertical lines
          that frame the active directory and of the character that is
          displayed to the left of a filename when it is tagged.  For
          best results, it should be a bright or distinctive color.

          ---------------------------
            OPTIONS | COLOR | ILINE    is the color of the
          ---------------------------  horizontal line that separates
          the inactive directory window from the directory information
          area below it.  It should be less bright or distinctive than
          the Alines color.

          -----------------------------
            OPTIONS | COLOR | HOT KEY    This is the color of the single
          -----------------------------  character (within a menu item)
          that you can press to choose a menu item.  For example, the
          "x" in "Exit" or "S" in "Sound".  For best results, it should
          be a color that stands out from the MENU color.

        All color settings you save via Options/Write may be overridden
        by the command-line switches /b and /r (see below).

        ------------------
          OPTIONS | PATH    This is the path to Double Directory's
        ------------------  executable and help files, dbldir.exe and
        dbldir.hlp.  It is used to find Double Directory's help file, to
        write the options to disk (see next section) and to execute Clear
        and run (see above).  If you are using DOS 3.0 or later, you can
        rename dbldir.exe to whatever you want.  Under DOS 3.0 or later,
        the Options/Path will be automatically set by Double Directory,
        but with DOS 2.x, you must set the path yourself (and you should
        not rename dbldir.exe).  The same restrictions apply as to
        Directory/Path above concerning valid path characters and length.

        -------------------
          OPTIONS | WRITE    Double Directory writes all of the Options
        -------------------  items (including View and Dir options) and
        the Directory/Sort fields and directions to Double Directory's
        executable file when you choose this option.  The next time you
        run Double Directory, the colors, view and sort settings and so
        on that you saved will be used.  Because it saves the options to
        the executable file, there is no need for a separate
        configuration file; thus, there is one less file to take up disk
        space and to transfer when you copy Double Directory to other
        disks and directories.  Be sure to read Miscellaneous/Viruses
        below and Options/Path above.

        The paths and masks current when you write the options to disk
        are not saved in dbldir.exe.  If you always want to start Double
        Directory with specific paths and/or masks, you can use a batch


                                                Double Directory  29

        file and pass the paths and masks via command-line parameters
        (see below).

                            ===========================
                              Command-line Parameters
                            ===========================

        You can add several command-line parameters (called switches) to
        the line you type when you run Double Directory.  Each switch
        affects some aspect of Double Directory when it runs.

        ------
          /s    The Skip switch causes Double Directory to skip (not
        ------  stop at) the title screen where you are prompted for new
        paths and/or masks (see above).  This is useful when included in
        batch files used to run Double Directory.  However, the
        unregistered version of Double Directory always stops at the
        registration screen, even if the Skip switch is used (we know
        this may be annoying, but we have to remind you to register).

        ------
          /b    Displays white on black for monochrome displays.  You do
        ------  not HAVE to use this if you are using a monochrome
        display.  This overrides any color settings you have saved via
        Options/Write.

        ------
          /r    Displays black on white (reverse); good for some LCD
        ------  displays found on portable computers.  This overrides any
        color settings you have saved via Options/Write.

        ------
          /p    The path must be in the form of drive, colon, back-
        ------  slash (/pa:\) or drive, colon, backslash, subdirectories,
        backslash (/pc:\work\march\); that is, it must end in a
        backslash.  You can put one or two path switches on the command
        line.  The path following the first path switch is used for the
        left directory window and the path following the second is used
        for the right window.  Thus, if you type "dbldir /pc:\bp\
        /pc:\gw\" Double Directory will display all files (because the
        default mask is "*.*") in the directory "c:\bp" in the left
        directory window and "c:\gw" in the right.

        ------
          /m    The mask must be in the form of name mask, period,
        ------  and extension mask.  The "*" character will let any
        number of characters pass through and the "?" character will let
        any one character pass through.  Thus, the mask "*.pas" will
        allow any entry with the "pas" extension pass through (appear in
        the directory).  "*.*" will let every entry pass through.
        "file.lt?" will let entries such as "file.lt1", "file.lta" and
        "file.lt$" pass through.  The default masks are "*.*".  So, if


                                                Double Directory  30

        you type "dbldir /m*.pas /m*.bas" only Pascal files will be
        displayed in the left directory window and only BASIC files in
        the right.

        The total length of the command line cannot exceed 124
        characters; this includes "dbldir" and all switches.  See the
        earlier sections of this manual and your DOS manual for more
        about masks and paths.

                                =================
                                  Miscellaneous
                                =================

        -----------
          Viruses    If you are using a program to prevent the spread
        -----------  of viruses on your disks, it may warn you about
        Double Directory.  These programs usually check whether a file's
        length or a calculated check sum changes.  When you save options
        (colors, paths, etc.) they are saved directly to the Double
        Directory file on disk; thus, there is no need for a separate
        configuration file.  Double Directory's length does not change.
        However, its check sum can change because the options can have
        many different values.  Therefore, you should inform the virus
        protection program that the contents of dbldir.exe can change
        (and thus its check sum) but not its length.


        --------------------
          Windows Updating    If the same complete path is displayed
        --------------------  in both directory windows and changes are
        made in the active window (you delete or rename a file, for
        example), the changes will also be shown in the inactive window
        (the directory will be reread).

        If the same drive (but not the same complete path) is displayed
        in both directory windows and some changes are made in the active
        window, they will be shown in the inactive window.  For example,
        deleting a file will increase the amount of free space on the
        disk so both directory windows will be updated.  However,
        renaming a file will not cause the inactive directory to be
        updated.

        -----------------------
          Memory Requirements    Double Directory will run in 272K RAM.
        -----------------------  It can handle about 275 entries in each
        directory window.  This is not enough memory to DOS/Shell, but it
        is enough to DOS/Clear and run.

        With 288K RAM, Double Directory can handle about 500 entries in
        each directory window.  This is enough memory to DOS/Shell and to
        DOS/Shell and Run some programs.


                                                Double Directory  31

        With 320K RAM Double Directory can handle 800 entries (its
        maximum) in each directory window.

        Fabrice Bellard's freeware program LZEXE is used to compress
        dbldir.exe from 160K+ to its current size.  When Double Directory
        runs, it loads into memory and then uncompresses itself.  This
        saves considerable disk space but adds less than a second to the
        time required to get it running.

        -------------------
          Necessary Stuff    WordStar, Word Perfect, Windows, and MS-DOS
        -------------------  are copyrighted and/or trademarked.

        The materials contained in the files dbldir.exe, dbldir.hlp and
        dbldir.doc are copyrighted (c) 1991, 1992, 1993 by George
        Tylutki.

                                    ========
                                      Tips
                                    ========

        -----------------------------------
          Easier Delete, Copy, Move, Etc.    Rather than scrolling
        -----------------------------------  through long directories to
        tag the files you want to work on (for example, to copy), you can
        let Double Directory do most of the work.  Be sure that
        Options/Confirm is set to Yes.  Press F7 to tag all of the files
        in the directory.  Choose the function you want to execute (copy,
        rename, etc.).  Double Directory will present each file name and
        ask you to confirm that you want to copy, rename, etc.  Confirm
        that you do or do not want to act on that file.  Since delete
        always asks you whether it should confirm each deletion (even if
        Options/Confirm is set to No), you do not have to set
        Options/Confirm.  Just press F7 and "D" and then confirm the
        deletion of each file you want to delete.

        --------
          Help    You can use Double Directory's View function to view
        --------  this manual if you find the help line and context-
        sensitive help information insufficient.  So, you may want to
        leave this manual (dbldir.doc) in the same directory with Double
        Directory until you are completely familiar with the program.
        You might also want to View this manual for information about an
        error message.

        After you become thoroughly familiar with Double Directory and no
        longer need context-sensitive help, you can delete (or rename)
        the file dbldir.hlp.  When Double Directory is run, it will look
        for but not find dbldir.hlp (it will not issue an error message).
        This will make an additional 11K of memory available for Shell
        and Shell and Run or to load TSRs and it will free up additional
        disk space.


                                                Double Directory  32


        -----------------------------------------
          Changing Drives & Directories Quickly    Putting the cursor bar
        -----------------------------------------  on a drive name and
        pressing Enter switches you to the root directory of that drive.
        This is useful to change drives and to jump up several levels
        from a subdirectory to the root directory.  Sometimes, however,
        it is  quicker to type in a path than to work down through
        subdirectories.  For example, typing "C:\budgets\home\march"
        might be easier and faster than using the cursor keys and
        pressing Enter and waiting for each subdirectory to be read from
        disk (especially with floppies).

        -------------------------------------
          Using Double Directory as a Shell    Using either Shell and run
        -------------------------------------  or Clear and run, you can
        use Double Directory as a shell or menu program.  That is, you
        can start your computer, run Double Directory, choose a file from
        the directory listing and run it.  When that program quits, you
        are returned to Double Directory and you can choose to run
        another program.  You can do this all day long always returning
        to Double Directory; you don't have to use the DOS command line
        at all to run programs, copy files, view files, and so on.  When
        you return to Double Directory, the same paths (using the same
        masks) will be displayed as when you left and it will not stop at
        the title screen (where you are prompted to enter new paths,
        masks, continue or exit).

        However, if you are using DOS 3.0 or later, you should use Clear
        and run rather than Shell and run because it removes Double
        Directory from memory (giving more to the program you want to
        run).  Start your computer and run Double Directory.  Tag the
        program you want to run and choose DOS/Clear and Run.  Double
        Directory will remove itself from memory and run the program.
        When the program ends, Double Directory will run again.  You can
        then run another program or use Double Directory to copy, delete,
        rename, etc. before shutting off your computer.  Each time a
        program ends that you have run via Clear and Run, Double
        Directory will run again.  Since Double Directory removes itself
        from memory when you Clear and Run a program, the program has
        access to all of your computer's memory (unlike with many other
        "shells"  which stay in memory and thus limit the memory
        available to the programs) except for a little bit required for
        batch processing.  DOS 3.0 or later is required for Clear and
        run.

        -----------------
          Quick Backups    If you regularly back up the files you have
        -----------------  just worked on at the end of each computer
        session (to floppy disks), you can do the following.  Set
        Options/Confirm to No.  Set one directory to your backup disk and
        the other to the directory that contains the files you want to


                                                Double Directory  33

        copy (make this the active directory window).  Compare the two
        directories by Date or Time.  Then press "C" to copy.  All of the
        files in the active directory that do not have matches in the
        other directory (your backup floppy) will be copied, because
        their dates and/or times are different (because more recent) from
        those on the backup floppy.  Just a few keystrokes make it easy
        to maintain frequent up-to-date backups of your files.


        ------------------------------
          Cleaning Up Your Hard Disk    Compare is also useful when you
        ------------------------------  are "cleaning up" disks (for
        example, removing files from your hard disk that are already on
        floppies).  After you compare the directories, if you select
        Dir/Toggle, all of the files that are in the working subdirectory
        AND on the backup disk will be tagged.  Now you can choose Delete
        to remove them from the hard disk.

        --------------------------
          Making Multiple Copies    Files remain tagged after you copy
        --------------------------  them; therefore, it is easy to copy
        files to several disks.  Put a disk in the destination drive; set
        Options/Confirm to No; tag the files you want to copy in the
        source directory; and press "C".  When all files have been
        copied, put another disk into the destination drive and press "C"
        again; the same files will be copied to the new disk.  This works
        only if each destination disk contains the destination path --
        for example, "b:\oldtext\".  This is simplest if the destination
        path is a root directory (a:\, b:\, etc.).

        -------------------------------------
          Copying/Moving to Different Disks    You can Move or Copy
        -------------------------------------  individual files from the
        source directory to several destination disks.  Let's say that on
        your hard disk there are 5 files you want to copy to several
        disks.  You want to copy "game.one" and "game.two" to your games
        floppy, "picture.a" and "picture.b" to your graphics floppy and
        "dbldir.exe" to your utilities floppy.  Set Options/Confirm to
        Yes.  Tag the 5 files.  Set the path of the destination directory
        to the appropriate path (for example, "b:\").  Put your games
        floppy in the destination drive.  Press "C" and then "Y" when it
        asks you to confirm that you want to copy "game.one".  Press "Y"
        when it asks you to confirm that you want to copy "game.two".
        After "game.two" is copied, remove the games disk from the
        destination drive and put in your graphics floppy.  Press "Y"
        when asked to confirm copying of "picture.a".  Press "Y" when
        prompted to copy "picture.b".  After "picture.b" is copied,
        remove your graphics floppy and put in your utilities floppy.
        Press "Y" to copy "dbldir.exe".  This works only if each
        destination disk contains the destination path -- for example,
        "b:\oldtext\".  This is simplest if the destination path is a
        root directory (a:\, b:\, etc.).


                                                Double Directory  34


        ---------------------------------
          A Double Directory Batch File    Double Directory always sets
        ---------------------------------  the paths for the two
        directories to the current path when it is run.  You can use the
        command-line switch /p to change either or both paths when you
        run Double Directory.  Further, you can create batch files so
        that Double Directory will read in specific directories for you.
        For example, you could create a batch file to run each time you
        finish word processing that would automatically read the
        directory that holds your word processing files and backup path.
        It might contain a line like this
           dbldir /s /pc:\wordstar\files\ /pb:\
        which would read the directories "c:\wordstar\files\" and "b:\"
        and skip the title screen.  (Of course, the unregistered version
        will stop at the registration screen even with the Skip switch.)

        ----------------
          Exit and Run    At the end of the day, you can use Double
        ----------------  Directory to clean up your disk(s) and then use
        DOS/Exit and run to run the last program of the day -- for
        example, to park your disk's heads or log the day's computer use.

        -----------
          Sorting    Place the cursor bar in the appropriate directory
        -----------  window and press "S" "D" "D" and the most recently
        created files will appear at the top of the directory listing.
        Press "S" "S" "A" and all of the drives and subdirectories in the
        current path will appear at the top of the directory listing.

        --------------------
          One Floppy Drive    If you have only one floppy drive, but want
        --------------------  to look at the directories of two floppies
        disks simultaneously, do the following.  Put the first disk in
        the drive and make it active (usually by highlighting "A:\" and
        pressing return).  Remove the first disk and put in the second.
        Switch to the other directory window and make the drive active.
        Now in one window you will have the directory listing of the
        first floppy disk and in the other directory window you will have
        the directory listing of the second.  You can switch between the
        two and scroll through either.  You can even Compare them.

        Double Directory is not designed to work with only one drive, but
        it can be used on such a system.  (We believe that NO system
        should have only one drive, which precludes easily making
        frequent back-ups.  If it's hard to make back-ups, they are not
        made.  If they are not made frequently, sooner or later you will
        meet with a disaster -- guaranteed.)  However, DOS will
        occasionally take over and display messages to switch disks; this
        will mess up the screen display.  Also, sometimes it will seem
        that nothing is happening (press the Enter key when this
        happens).  You can clean up the display by choosing Options/Rows


                                                Double Directory  35

        and either "2" or "4" which always clears the display before
        changing display modes.  You do not have to change modes; that
        is, you can choose "2" even if you are currently in 25-row mode.

                                 ==============
                                   Keystrokes
                                 ==============

        -----------------
          Function Keys
        -----------------
        F1 = context-sensitive help         F7  = tag all files
        F2 = information screen             F8  = untag all files
        F3 = quit Double Directory          F9  = reread directory
        F6 = go to other directory window   F10 = main menu

        ------------
          Hot Keys
        ------------
        A = compare directories             M = change directory mask
        B = change file attributes          N = rename file
        C = copy file                       O = DOS
        D = delete file                     P = change directory path
        E = reread directory                R = remove subdirectory
        F = display information             S = sort directory
        H = general help                    T = options menu
        I = directory menu                  V = move file
        K = make subdirectory               W = view file
        L = file menu                       X = exit Double Directory

        -----------------
          WordStar Keys
        -----------------
        Ctrl-S = left arrow                 Ctrl-D = right arrow
        Ctrl-E = up arrow                   Ctrl-X = down arrow
        Ctrl-R = page up                    Ctrl-C = page down
        Ctrl-H = backspace                  Ctrl-Y = delete line (Del)
        Ctrl-Q+R = Home                     Ctrl-Q+C = end

        --------------
          Other Keys
        --------------
        / = main menu                       Ins = tag file
        Del = untag file                    Spacebar = toggle tag
        Enter = choose a directory
        Esc = cancel (go back 1 step)
        Scroll Lock = scroll both directories
        Shift-F7 & Shift-F8 = toggle file tags in active directory
        Shift-F10 = cancel all (go back all steps)
        Left & Right Arrow = go to other directory window
        Ctrl-S, Ctrl-D = go to other directory window
        Tab, Shift-Tab = go to other directory window


                                                Double Directory  36

                               ==================
                                 Error Messages
                               ==================

        Error numbers may be positive (5) or negative (-7).


        Access denied.  Is directory empty? [5]
          You have attempted to Remove a directory that still contains
          files or subdirectories.

        Both paths are invalid.  [-1]
          If at the title screen, you changed both paths and both are
          invalid.

        Can't remove files, drives, parent directory for Volume ID. [-6]
          You have tried to Remove a subdirectory and the cursor bar is
          not on a subdirectory name.

        Cannot copy/move file(s); source = destination. [-13]
          You can copy or move files only between different paths.  It
          makes no sense to try to copy a file from a: to a:.

        Cannot tag drives, subdirectories or volume labels. [-25]
          See the section TAGGING FILES above.

        Context-sensitive help not available.
          If you want context-sensitive help, but when you press F1 you
          get this message, the Options/Path is not set to the path to
          the file dbldir.hlp.  This can occur sometimes when you write
          options (which saves the path) and then move dbldir.exe and
          dbldir.hlp to a different path (drive and/or subdirectory).
          Reset Options/Path.

        Clear and Run requires DOS 3.0 or later. [-19]
          See File/DOS/Clear and run.

        Device fault. Printer on? [25]
          Probably you're trying to print when your printer is off or
          off-line.

        Directory size must be between 28 and 800. [-17]
          See Options/Dir/Size.

        Disk full. [61]
          See File/Copy above.

        Double Directory help file not loaded.  See Context-sensitive
          help not available.

        Drive not ready. [71]
          Probably a floppy disk drive door is open.


                                                Double Directory  37


        Error reading disk. [-3]
          This might occur, for example, when Double Directory tries to
          read a disk and can't obtain the number of free bytes.

        Error reading/writing configuration options (filename). [-8]
          When reading (when the program first runs) or writing the
          configuration options, Double Directory was unable to find or
          open dbldir.exe or dbldir.exe does not contain valid
          configuration information.  Options/Path may not be set
          correctly.  See also Options/Write.

        Error saving options; EXE file may be corrupted. [-9]
          Some error occurred while writing configuration options to
          dbldir.exe.  Dbldir.exe may have been corrupted.  You should
          not use it again; make a new copy of dbldir.exe from your
          backup disk.

        43/50 rows not available with your display adapter. [-7]
          An EGA or VGA is required.

        File is not tagged. [-26]
          See the section TAGGING FILES above.

        File not found. [2, 53]
          This message can appear if you switch disks when renaming a
          file; Double Directory is unable to find the file to rename.

        I/O error. [57]
          Unspecific error when reading a disk.  Try again or try another
          disk.

        Must be .exe, .com or .bat file. [-11]
          To Shell and run, Clear and run, or Exit and run, you must tag
          an .exe, .com, or .bat file.

        No files tagged. [-5]
          You have tried to copy, delete, rename, etc. a file and none
          are tagged.

        No path specified. [-2]
          You have manually entered an invalid path (Path not found) and
          then tried to do something like Make directory.

        Not enough memory. [7]
          If you attempt to set Dir/Size (see above) too large.

        Options/Path must be set before Options can be saved. [-20]
          If you are using a version of DOS prior to 3.0, you must set
          Options/Path before attempting to write configuration options
          to disk.


                                                Double Directory  38

        Out of string space. [14]
          This may occur when you first run Double Directory.  It means
          that there is not enough room to run the program (it can load
          but not run).

        Path/File access error (does it already exists?). [75]
          You have attempted to Make a subdirectory and a file or
          subdirectory with the same name already exists on the disk.

        Path not found. [3, 76]
          You have manually entered an invalid path or the problem that
          is discussed in the Technical Note in Directory/Path has
          occurred.

        Print available only while viewing a file. [-16]
          See Options/View/Print.

        Unable to delete file to be replaced. [-10]
          This should occur only if Double Directory is unable to obtain
          the file attributes of the file to be deleted.

        Wrap column must be between 1 and 999. [-14]
          See Options/View/Wrap.

        Wrong help file version (dbldir.hlp). [-15]
          You shouldn't see this message.  Future versions of Double
          Directory's help files may have different formats.

        _ entries read; there may be more in this directory. [-4]
          See Options/Dir/Size.

        These two errors might occur when printing.
        Device timeout. [24]
        Out of paper. [27]

        You should never see any of the following:
        No files found. [18]
        Bad file mode. [54]
        File already open. [55]
        FIELD statement active. [56]
        File already exists. [58]
        Bad record length. [59]
        Input past end of file. [62]
        Bad record number. [63]
        Bad file name. [64]
        Too many files. [67]
        Device unavailable. [68]
        Communication-buffer overflow. [69]
        Permission denied. [70]
        Disk-media error. [72]


                                                Double Directory  39

                                    =========
                                      Index
                                    =========

         :  18                                Hot keys, 28
         ?  19, 29                            Inactive directory cursor, 27
         .  19                                Inactive directory frame, 28
         ..  9, 11, 18, 19                    Left directory window, 27
         [] 22                                Menu cursor, 27
         *  19, 29                            Menus, 27
         \  18                                Names, 27
                                              Right directory window, 27
                                              Sample text, 27
         /b, 29                               Tag character, 28
         /m, 29                               Window, 26
         /p, 29, 34                         Command line
         /r, 29                               DOS, 32
         /s, 29                               Double Directory, 8, 28, 29,
                                              30, 34
         .bat, 17, 18                         Shelling, 12, 17, 18
         .com, 17, 18                       Command.com, 16, 17
         .exe, 17, 18                       Compare directories
                                              Date, 20
        <drive>, 9                            General, 19, 34
        <parent>, 9, 18                       Name, 19
        <subdir>, 9, 18                       Size, 20
        <vol id>, 9                           Time, 20
                                            Configuration file, 28, 30
        Active directory, 10, 12, 14, 33    Confirm, 9, 12, 13, 14, 15, 18,
        Active directory window, 21           21, 22, 31, 32
        ASCII, 24                           Context-sensitive help, 8, 31,
        ASP, 6                                36
        Association of Shareware            Control characters, 24
          Professionals, 6                  Copy, 14, 16, 33
                                            Cotton Software
        Backslash, 18, 29                     Address, 6, 8, 44
        Batch file, 17, 28, 29, 34            Phone number, 1, 8
        Browsing, 15                        Cursor bar, 10

        Cancel, 11, 14, 15                  DBLDIR.DOC, 4
        Carriage return, 24, 25             DBLDIR.EXE, 3, 4
        Clear and run, 17, 28, 30, 32       DBLDIR.HLP, 3
        Clip and Save, 7, 44                DBLDIR.ICO, 4
        Cluster size, 22                    Default mask, 19, 29
        Color                               Delete, 13, 14, 15, 31
          Active directory cursor, 27       Destination directory, 10, 14,
          Active directory frame, 28          33
          Background, 26                    Destination disk, 33
          Blink, 26                         Destination drive, 33
          Cursor, 10                        Destination path, 15, 33
          Foreground, 26                    Directory
          Help text, 27                       Changing, 11


                                                Double Directory  40

          Make, 21                          Filter, 19, 24
          Options, 23                       Free bytes, 22
          Remove, 21                        Free disk space, 22, 30, 31
          Root, 32                          Free memory, 22
          Size, 23
          Time, 23                          Have You Read That Movie?, 44
        Directory information area, 9,      Help
          28                                  Context-sensitive, 9
        Directory window, 9, 18, 19, 30       Context-sentitive, 3
        Display adaptors, 3                   Cotton Software, 8
        Display width, 25                     Error, 36
        Documentation                       Help line, 9, 31
          Printing, 4                       Help text, 13
          Reading, 4
        DOS                                 Inactive directory, 14
          Clear and run, 17                 Inactive window, 10, 30
          Exit and run, 18                  Information screen, 22
          Shell, 16                         Installation, 3
          Shell and run, 17                 International orders, 8, 44
        DOS 2.0, 3, 28
        DOS 3.0, 3, 28, 32, 36, 37          Keys
        DOS commands, 16                      "/", 9, 10, 12
        DOS mode command, 26                  "2", 22, 35
        DOS problem, 19                       "4", 22, 35
        Double Directory                      "B", 15
          $dbldir$.bat, 17                    "C", 14
          Compressed, 31                      "D", 13
          dbldir.doc, 31                      "E", 21
          dbldir.exe, 13, 22, 28, 30          "F", 22
          dbldir.hlp, 13, 17, 28, 31,         "H", 13, 27
          36, 38                              "I", 13
          Path to dbldir.exe, 28              "K", 21
          Renaming dbldir.exe, 28             "L", 12
          Running, 3                          "M", 19
        Double Directory package, 7           "N", 13
                                              "O", 16
        Editing, 13                           "P", 18
        EGA, 22                               "R", 21
        Entering text, 12                     "S", 20
        Evaluation, 7                         "T", 13
        Evaluation period, 8                  "V", 14, 15
        Exit, 9, 16, 17, 18                   "W", 24
                                              "X", 18
        F1, 27                                Arrow, 9
        F7, 31                                Backspace, 12
        File Attributes                       Complete list, 35
          Archive, 15                         Cursor, 10, 11
          Hidden, 15                          Del, 11, 12, 15
          Read only, 15                       Direction, 10
          Setting, 15                         Editing, 12
          System, 15                          Enter, 9, 11, 16
          Viewing, 23                         Esc, 11, 14, 15


                                                Double Directory  41

          F1, 8                               Info, 22
          F10, 9, 10, 12                      Main, 9, 12
          F2, 14, 22                          Make, 21
          F3, 18                              Mask, 19
          F6, 10                              Move, 15
          F7, 12, 21                          Options, 13, 22
          F8, 12, 21                          Path, 18, 28
          F9, 16, 21                          Remove, 21
          Function, 12                        Rename, 13
          Hot, 10, 12                         Rows, 22
          Ins, 11, 15                         Sort, 20
          Scroll Lock, 10                     Sound, 22
          Shift-F10, 11, 14                   Tag, 21
          Shift-F7, 12, 21                    Title, 9
          Shift-F8, 12, 21                    View, 14, 24
          Shift-Tab, 10                       Write, 28
          Spacebar, 11                      Menu bar, 9, 10
          Tab, 10                           Messages
          WordStar, 10                        Error, 13, 14, 15, 21, 22, 23,
                                              31
        LCD displays, 29                      Informative, 14, 23, 34
        Left arrow character, 10, 14        Microsoft Windows, 4
        Left directory window, 29           Minimum Requirements, 3, 30
        Licensing, 7, 8                     Miscellaneous, 30
        Line feed, 24, 25                   Monochrome display, 27, 29
        Line truncate, 25                   Move, 15, 33
        Line wrap, 25
        LPT1, 26                            Network, 16
        LZEXE, 31
                                            Ombudsman, 6
        Mask                                Overwrite file, 14
          Changing, 8, 19
          Command-line switch, 29           Parent directory, 9
          Default, 8                        Path
          Length, 19                          Changing, 8, 11, 18
        Maze Survey, 44                       Command-line switch, 29
        Memory, 16, 17, 23, 24, 30, 31,       Default, 8
          32                                  DOS, 3
        Menu                                  Length, 19
          Attributes, 15                      Source, 15
          Color, 26                           To Double Directory, 28
          Compare, 19                       Point and shoot, 18
          Confirm, 22                       Print
          Copy, 14                            Entire file, 26
          Delete, 13                          Part of file, 26
          Directory, 13, 23                 Printer, 26
          DOS, 16                           Printing, 11, 14, 25
          Exit, 18                          Printing
          File, 12                            cancel, 26
          File tag, 15                        pause, 26
          General, 9, 10
          Help, 13                          Quick reference, 35


                                                Double Directory  42

        Quit, 18                              Character, 11
                                              Directory, 12, 31
        Registering, 5                        File, 11, 33
        Registration, 6                     Technical Note, 16, 17, 19, 23
        Registration                        Telephone and mail support, 7
          benefits of, 6                    Time, 16, 23
        Registration fee, 6, 8, 44          Tips
        Registration form, 44                 "Cleaning up hard disk", 33
        Registration screen, 29, 34           Backups, 32
        Rename, 13                            Batch files, 34
        Replace file, 14                      Changing directories, 32
        Reread, 16, 30                        Comparing directories, 33
        Right arrow character, 10, 14         Copying/Moving, 33
        Right window, 29                      Delete, copy, etc., 31
        Root directory, 9, 33                 Exit and run, 34
        Rows, 22, 34                          Help, 31
        Run another program, 16               Multiple copies, 33
        Run tagged file, 17, 18               One drive, 34
                                              Shell, 32
        S, 10                               Title screen, 8, 18, 29, 32, 34
        Saving Options, 28                  Toggle
        Screen, 9                             File tags, 11, 15, 21, 33
        Scroll, 10, 14, 31
        Scroll character, 10                Untag
        Shareware, 5, 6, 7                    Directory, 12
        Shell, 16, 17, 30, 32                 File, 11
        Shell and run, 22, 23, 30, 32       Updates
        Skip file                             Discounts, 7
          See Confirm, 13                     Notification, 7
        Skip switch, 29, 34
        Smiley-face cursor, 26              Valid drives, 9
        Sort                                Valid filename, 12
          Ascending/Descending, 20          Valid mask, 12, 19
          Date, 20                          Valid path, 12, 18
          Extension, 20                     VGA, 22
          General, 20                       View
          Name, 20                            Cancel, 11
          No sort, 21                         Defaults, 24
          Size, 20                            End of line, 25
          Time, 21                            File, 14
        Sound, 22                             Line truncate, 25
        Source directory, 10, 14, 33          Line wrap, 25
        Space character, 24                   Print, 24, 26
        Subdirectory, 9, 12, 15, 17           Show control characters, 24
        Support, 8                            Show CR/LF, 24
        Support                               Strip high bit, 24
          Mail, 8                             Wrap column, 25
          Telephone, 8                      View window, 14
        Switches, 29, 34                    Viruses, 30
                                            Volume name, 9, 11, 15
        Tab, 24
        Tag                                 Warranty, 7


                                                Double Directory  43

        Window
          Color, 27
          Directory, 9
          Directory information, 9
          Help, 8, 9
          Informative, 22
          Menu, 9
          View, 14
        Windows
          Microsoft, 4
        Word Perfect, 25
        WordStar, 24, 25




             REGISTRATION FORM                  Date:_________________


        Send me (1) a registered copy of Double Directory, (2) a copy of
        Clip and Save and (3) a copy of [] Maze Survey OR [] Have You
        Read That Movie? (see PRODUCTS.DOC for descriptions).




         Register Double Directory ($15.00 per copy)   $________

                  International orders (add $3.00)     $________

                                              TOTAL    $________


               [] Check           [] 5 1/4" disk

               [] Money order     [] 3 1/2" disk

        Total includes shipping, handling and taxes where applicable.
        International orders U.S. Dollars please.

        Name _________________________________________________________

        Street _______________________________________________________

        City ______________________________ State ____  Zip __________


        Please provide the following information.  I obtained my copy of
        Double Directory from:

        [] Shareware distributor ________________________________
        [] Electronic bulletin board ____________________________
        [] Users' group _________________________________________
        [] Other ________________________________________________
        [] Friend, colleague, relative

        Suggestions/comments: ________________________________________

        ______________________________________________________________

        ______________________________________________________________

        ______________________________________________________________

        Send to: 100% Cotton Software
                 RR 1 Box 1622
                 Hop Bottom, PA 18824