PAGE 1    WALDEE-WOOD Telescope Parameter Program -- Version 2.1
          SHRSCOP.DOC -  Document File for the Shareware Edition
       Copyright (c) 1993 - Stephen R. Waldee; All Rights Reserved.

    INSTRUCTIONS FOR USE:
    (a) Computer/Monitor & Installation

         Version 2.1 of this program, optimized for color monitors but also
    usable on monochrome monitors, should work on any DOS-compatible personal
    computer with at least 384K ram (the program has been tested and found to
    run with less than 300 kbytes of available memory) on DOS 2.0 and later.
    The user is provided with information for selecting magnification
    ranges of an optical telescope for visual astronomical observing.

         The program is applicable to any kind of visual telescope, from a
    terrestrial "spotter" to an observatory instrument, as long as it employs
    interchangeable eyepieces of standard focal lengths and apparent fields,
    and has an aperture up to 17 inches (26 inches in the registered version.)

           The program may be run directly from the floppy disk by typing
    SHRSCOPE at the DOS prompt.  The diskette should contain the files:

         1.  SHRSCOP.DOC --  information ASCII text file of the
               program manual
         2.  DEF.DOC -- information ASCII text file of definitions
         3.  REG.DOC -- information ASCII text file about registering
               the program
         4.  ORDER.DOC -- ASCII text file with registration order form
         5.  SHRSCOPE.EXE -- executable program file
         6.  README.DOC -- text file describing the program.

         This program must not be transmitted as shareware in any form
    unless ALL of the above files are included.  You must register this
    program if you wish to continue to use it after the 30-day evaluation
    period.  You may license either this Shareware edition, or obtain a copy
    of the commercial expanded version of "SCOPE - The Waldee-Wood Telescope
    Parameter Program" (c) which offers many more features.  Please read the
    "Registration Info" file reg.doc, which is accessible from the help menu
    by selecting option <r>.

         Before using the program disk, make a backup copy.  You will need
    the program disk and a fresh blank floppy of the SAME type as the
    original program disk: either a 5-1/4" double-sided, double-density
    360K floppy, or a 3-1/2" double-sided, double-density 720K floppy
    (also called "2S-2D" or "DS-DD".)  Read carefully all the way through
    the following paragraphs BEFORE attempting to copy or install the
    program!

         If you have only one floppy drive, put the original program disk
    into the drive and get the A> prompt.  Then type
             DISKCOPY A: A:
    and press the <ENTER> key.  DOS will prompt you when to take out the
    original disk and when to put in the blank floppy.


PAGE 2

        If you have two floppy drives, then put the original program disk
    into Drive A and the blank floppy into Drive B.  Get A> and type
             DISKCOPY A: B:
    and press the <ENTER> key.  DOS will not only copy all the files, but
    also will copy the formatting of the diskette, so that the blank floppy
    need not be formatted in advance.

        BE SURE YOU ARE USING THE SAME CAPACITY BLANK DISKETTE!  If you are
    not, then the copying process will be halted by DOS.  If you do not
    have a double-density blank disk for your copy, then you must copy all
    of the files onto a formatted diskette.  Either copy the files one at
    a time, or use the *.* command; refer to your DOS instruction book for
    all of the details of making copies of files between disks.

         To run the program directly from the floppy disk, type SHRSCOPE at
    the floppy disk A> DOS prompt.  Once the program and help files are
    loaded, SCOPE works just as fast from the floppy as from a hard disk.

         All files MUST be present on the disk or the subdirectory for
    running the program.  To install SHARESCOPE on a hard disk, copy all
    the files into the same hard disk subdirectory; we suggest assigning
    it the name SCOPE.

         If you are unfamiliar with procedures for making subdirectories,
    consult your DOS manual for details; in brief:

         (1) Go to the root directory of the desired drive.  If
             drive is called C, then at the DOS prompt, type
                 C:
             and press the ENTER key.  At the C> prompt, type
                 cd\
             and press the ENTER key.

         (2) Type the following if you wish to name the subdirectory
             "SCOPE" -
                 mkdir SCOPE
              and then press the ENTER key.

         (3) Enter the directory SCOPE by typing
                 cd\SCOPE
             and pressing the ENTER key.

         (4) Place the floppy disk containing the program in the
             floppy drive (in this example, called A drive.)
             Type the following
                 copy a:*.*
             and press the ENTER key.

         (5) After the files have been copied, run the program by
             typing
                 SCOPE
             and pressing the ENTER key.


PAGE 3

         If difficulties are encountered, refer to your DOS manual or other
    appropriate reference book; you may run the program directly from the
    floppy if desired.

    (b) Entering Data Into the Program

         When prompted, you must type in the information requested.  If you
    make a typing mistake, the request will be repeated or an error "beep"
    will be audible.  Note carefully what you type: the program will lock
    out errors and will not proceed until usable information is provided.
    Thus, if you are asked for a numerical value, do not type any characters
    other than numbers.

         Following standard software convention, the program uses brackets
    (<...>) to indicate certain numbers or letters that you must type:
    do NOT type the brackets themselves, but type only the letters or
    numbers indicated inside them in the examples.

         Hit the <ENTER> key (sometimes called the <RETURN> key on older
    keyboards) only when requested, such as at the end of a numerical value
    for your scope aperture.  At other times, if a single letter is required
    like "s" for "similar magnitude," the <ENTER> key is not necessary, and
    will not be requested.   You may type either upper or lower case letters.

         In general, the authors have tried to be understanding and
    compassionate to users who are not Grand Wizards of the computer!
    We hope that the program's prompts and procedures require little or
    no explanations beyond the information presented on the screen.

         For users who are not experienced with telescope optics, we
    suggest you read the Definition file and look up the entries for
    aperture, focal length, focal ratio, eyepieces, and apparent field.
    Typical values for each of these subjects will be detailed in the
    individual definition.

        If you would like to "try out" a sample telescope system, you
    might enter the data for the following telescope and eyepieces,
    following the on-screen prompts after you start the program:

        TELESCOPE APERTURE:                   8 inches (or 203 millimeters)

        TELESCOPE FOCAL LENGTH:               2032 mm
           or
        TELESCOPE FOCAL RATIO:                f/10

        1.25" BARREL EYEPIECE FOCAL LENGTH:   26 mm

        1.25" BARREL EYEPIECE APPARENT FIELD: 50 Degrees.

        This is a very typical amateur telescope combination representing
    an 8-inch aperture Schmidt-Cassegrain telescope and an eyepiece that
    offers moderate powers for deep-sky viewing.  Or you may request a
    power of about 77X, which requires nearly the same eyepiece focal length.


PAGE 4

    (c) Features of the Current Version of the Program

        The unregistered trial version of the program included on this disk
    will calculate amateur visual telescopes up to 17 inches aperture.  The
    optical formulas used are in large part the "textbook" values, determined
    by the laws of optics and the characteristics of light wave behavior.
    In a few cases the formulas are "rule of thumb" subjective values that are
    accepted by knowledgeable and experienced visual astronomers.  Licensed
    and registered versions of this shareware edition support apertures up to
    26 inches, and will print charts of the system screen of optical perfor-
    mance; unregistered copies do NOT support any kind of printing.

        This current Shareware Version 2.1 corrects some small errors in
    the original shareware demo edition, and provides some of the upgraded
    menus in the registered and commercial versions.  Two other versions of
    this program are available: the full expanded commercial program "SCOPE"
    with many more features, and the special upgrade "Observatory Red"
    color edition for registered users of the commercial version, offering
    red text on a black background for night use at the telescope.  Consult
    the "Registration Info" file reg.doc, readable from the Help menu by
    selecting option <r>.

        Before running the program, the user has the option of reading
    the help files: this program manual, the definitions of astronomical
    terms relevant to the program and to observing, and the registration
    information file.  If the program is used beyond the 30-day evaluation
    period, it must be registered to obtain a permanent license for use.
    Over one thousand hours of program development have gone into the
    editions of this program, which will continue to be upgraded as long
    as user support is provided.

         The user must supply the following information in order to
    run the program:

      (1) The telescope light-gathering aperture in inches or millimeters;

      (2) The telescope's focal length in either inches or millimeters,
          or the focal ratio;

      (3) The focal length in millimeters of the eyepiece selected;

      (4) And finally, the eyepiece's apparent field of view in degrees,
          or the desired eyepiece type.

         The apparent field specification is almost always provided
    by the eyepiece manufacturer.  If it is not known, a database of
    information representative of general characteristics of over 60
    standard eyepieces is searched to find a close match to the desires
    of the user.  Since different manufacturers use varying methods for
    specifying this parameter, the actual visual eyepiece field, sometimes
    called "true field" or "real field," may not always be accurately
    calculated from the apparent field parameter.  Thus, this program does
    NOT intend to calculate the "True Field" as will be described below.


PAGE 5

         If a commercial eyepiece of the type specified is available at
    the focal length specified, the options list will include that type of
    eyepiece for calculations with the telescope.  A complete menu of
    configuration options for selecting the size of eyepiece barrel/scope
    focuser is presented at the beginning of the program.

         After initial data input, the program will calculate the following
    system parameters:

    -LIGHT GRASP VERSUS THE UNAIDED EYE: the amount of light gathered
    across the area of the telescope objective versus the light gathered
    across the area of the dark-adapted eye's entrance pupil of 7 mm.

    -FOCAL RATIO: the ratio of the aperture to the focal length, which
    may be effectively increased with the introduction of a Barlow lens.

    -TELESCOPE POWER OF MAGNIFICATION: shown with warnings if the
    magnification exceeds typical observing conditions.

    -POWER PER INCH OF APERTURE: the magnification per inch of the
    diameter of the objective, a good indication of appropriate
    magnification range for a given aperture.

    -EXIT PUPIL: the measure of the diameter of the image of the
    objective presented at the output of the eyepiece, intended to enter
    the "entrance pupil" of the observer's eye.  The maximum entrance
    pupil of the dark-adapted eye is assumed to be about 7 mm, so a
    telescopic exit pupil much in excess of this will cause a loss of
    light, in effect reducing the effective aperture of the telescope.

    -ESTIMATED WIDEST FIELD OF VIEW: the program checks the eyepiece
    barrel size and then scans the ocular database for the lowest
    practical magnification available that will provide an exit pupil
    as close to 7 mm as possible.  When the eyepiece is selected, the
    visual field of view is estimated for that eyepiece; thus the value
    changes if the focuser barrel size is switched from 1.25" to 2.00"
    eyepiece barrel size, permitting a wider potential field of view.
    For example, the popular 8" Schmidt-Cassegrain will achieve its low-
    est potential power, widest field, and largest exit pupil with 2.00"
    eyepieces, not the smaller 1.25" barrel sizes.  The estimated calcula-
    tion of wide field must be verified by actual scope star-field tests!

    -APPROXIMATE VISUAL FIELD: in arcminutes, of the telescope/eyepiece
    combination at the power specified; due to differences in the eyepiece
    makers' methodology in measurements, this specification may not always
    agree with the precise, flat "true field" of the eyepiece.  The true
    field is always best determined by actual measurements of a calibrated
    chart or by measuring the drift of a known star field through the
    eyepiece field.  However, the actual differences (if any) between
    the approximate visual field and the true field will probably be
    minimal if the eyepiece specifications are accurate.


PAGE 6

    -VISUAL STELLAR MAGNITUDE LIMIT: of a point-source star image,
    with compensations for skyglow, assuming that the observer's eye
    is dark-adapted.  The default value is 6.5 magnitude naked-eye limit
    for a dark sky offering good opportunities for perceiving faint
    stars and nebulae.

         The visual limiting magnitude will be displayed during any
    power chosen for the optical system, but it may only be achieved
    visually by employing enough magnification to be equal to the
    diameter of the telescope aperture in millimeters.  Then the star's
    "Airy disk" is sufficiently large to register on the retina, and the
    magnification provides contrast by dimming the background light.

         This specification does not directly indicate the visibility of
    non-stellar "extended" objects like nebulae or galaxies, but is useful
    in comparing scope/sky efficiencies.

        Your scope may perform worse than the prediction if the optics are
    dirty or poorly coated, or if the actual sky darkness differs from your
    chosen naked-eye limiting magnitude.  Conversely, your scope may actually
    outperform the prediction if you use a high-efficiency small refractor
    without a diagonal, if your reflector's mirrors have "enhanced" coatings,
    and if you use the best quality low-loss coated eyepieces, or if your
    sky is darker than 6.5 naked-eye magnitude.

        The commercial edition of "SCOPE" provides options for customizing
    the user's actual sky conditions to the program's magnitude calculation.

    -RESOLUTION [Dawes' Limit]: taken from the famous 19th century British
    amateur astronomer Reverend William Rutter Dawes' measurement of percep-
    tions of the minimum separations in arcseconds of close similarly-bright
    double stars in the 5-7 magnitude range, determined with small refractor
    telescopes.

        This criterion may not represent the potential performance of short-
    focus reflectors or telescopes with misaligned or poor optics.  However,
    in some cases the Dawes limit may be exceeded with excellent optics on
    very good observing nights.

    -CLOSEST SIMILAR DOUBLE STAR OBSERVABLE AT A GIVEN POWER WITHOUT
    ATMOSPHERIC LIMITS: a calculation of the closest detectable separation
    at the system's operating magnification of a typical Dawes double, based
    on the assumption that the naked eye is just able to detect a separation
    of 4 arcminutes (or 240 arcseconds.)  This is a theoretical calculation,
    assuming excellent optics and no atmospheric distortion.  The formula
    employed was confirmed by the experience of observers with excellent
    telescopes, viewing under steady skies which occasionally permitted
    splitting double stars close to 0.5 arcsecond separation.

    -LIGHT POLLUTION REDUCTION and NEBULAR LINE BANDPASS FILTER
    SPECIFICATIONS: if chosen during the program start-up, the System Screen
    report will list the options of employing light-pollution-reduction (LPR)


PAGE 7

    or various kinds of nebula bandpass filters if the exit pupil is within
    range, helpful for learning the conditions for using each filter.

    (d) Helpful Operating Guides and Error Reports

      (1) Magnification Limits

        Some operating conditions will flag a warning that certain limits
    have been exceeded.  For example, it is assumed for a small scope of,
    say, 3" aperture, that 50 power per inch of aperture is the practical
    limit for a resolved image of an extended object such as a planetary
    or lunar surface detail, and that 60 power per inch of aperture is the
    maximum magnification needed to see the closest double stars.

        Beyond these values of magnification, the wave nature of light
    limits the resolution of the image, which will become larger and larger,
    but fuzzier and fuzzier as the power is increased.  However, very large
    aperture telescopes will almost never be used at or above 50 power per
    inch of aperture, due to atmospheric limitations.  A sliding scale is
    provided for judging the appropriate power per inch of aperture as the
    aperture increases, utilizing the maximum power that the best atmos-
    pheric conditions will permit.

        The observer may be enticed to use high powers in excess of 1,000
    that William Herschel or S. W. Burnham occasionally utilized for special
    observations, but most amateur astronomers with telescopes of, say, 8"
    of aperture can never hope to employ more than 300 to 400 power; on some
    nights of unsteady air, only the lowest powers provide clean images.

     (2) Resolution

       In larger scopes it is generally asserted that the best nights of
    viewing will permit a resolution of no more than about 0.5 arcseconds,
    although there may indeed be a few nights per year when the "seeing"
    exceeds this value at high viewing altitudes, if the aperture of the
    instrument is within range.  Users of very large observatory scopes have
    sometimes been able to split doubles of as little as 1/4 arcsecond
    separation, but this is not a common experience with amateur scopes!

     (3) Exit Pupil

       When the telescope magnification is too low, generally below 3 to 4
    power per inch of aperture, the "exit pupil" of the optics will be too
    large for the dark-adapted eye, causing some of the image of the full
    telescopic aperture to spread out beyond the area of the eye's "entrance
    pupil," with a loss of effective aperture.  In a scope with obstructed
    aperture (a Newtonian reflector or Schmidt-Cassegrain, for example) an
    overly-large exit pupil will often force the user to dodge the dark blob
    in the center of the field caused by the secondary mirror.  However,
    refractors or other non-obstructed telescopes may be used with over-
    large exit pupils in order to gain very wide fields at the expense
    of image brightness and contrast.  The program will display a warning if
    the exit pupil exceeds the typical maximum of about 7.5 mm.


PAGE 8

     (4) Focal Ratios

       Typical real-world visual telescopes are usually constructed to be
    within a focal ratio range from as low as f/3 (rich-field types) to as
    high as f/30 (solar telescopes) although these values are exceeded in
    eyepiece projection photography and in the construction of certain types
    of telescopes such as schiefspieglers.  This program assumes during scope
    scope data input that anything below f/1 or over f/30 represents mistaken
    parameters, and will suggest checking for errors.

     (5) Viewing Suitability

        Based on the telescope/eyepiece combination chosen by the user,
    the program makes some brief suggestions about appropriate astronomical
    subjects in general detail, as a guide to beginners, in order to help
    dispel incorrect expectations about telescope performance.  Of course,
    good dark skies are necessary for "richfield" starcloud sweeping or
    for discerning galaxies and nebulae.  If the magnification and exit
    pupil are within range, the program alerts the user when light-
    pollution and nebular filters most effectively may be employed.

     (e) Menu Options

        At the end of the performance data screen, the option is available
    to enter new eyepiece parameters, to change the telescope, to add a
    Barlow lens to the system or to change or remove it, to view double
    stars, to turn on or off the filter information, to get a specific power
    of magnification, or to exit to DOS.  The commercial version "SCOPE"
    offers many other options, detailed in the "Registration Info" file
    which may be accessed from the help menu by choosing option <r>.

     (1) View Double Stars

       A handy option is the calculation of power needed for the
    splitting of a defined double star separation.  If the double is
    closer than 0.5 arcseconds an alert is reported, as most users
    may never encounter sky conditions and optical perfection that
    will permit splitting this separation.  The function defaults to
    the "no Barlow" mode at startup, and the nebular filter data are
    turned off during the double star mode.

       When the double star separation is entered, the program will
    round off values under 1/10th arcsecond, since visual resolution of
    such fine detail is virtually impossible.  Next, options are given
    for choosing magnifications for detecting different kinds of doubles.

       The classic Dawes double -- a similarly colored pair of medium
    magnitude stars -- may be split by most observers when the magnifi-
    cation employed boosts the double's separation to about 4 arcminutes
    (or 240 arcseconds) in the eyepiece field.  For doubles of widely
    differing magnitudes, the program offers higher magnifications to
    further open up the doubles' separation.


PAGE 9

        If the double is below the Dawes limit of the scope aperture
    another error is noted, allowing the user to define a larger double.
    If the double can be split with the lowest power eyepiece, the program
    will install an eyepiece in the barrel size defined that will give
    the largest usable dark-adapted exit pupil size equal to or less
    than 7.5 mm.  If the double is very wide but within 2/3rds of the
    widest possible visual field, the program will use the lowest power
    range of the scope consistent with an exit pupil less than 7.5 mm,
    and choose the widest-field eyepiece.

       If the magnification needed requires the use of Barlow lenses,
    the program will automatically install and test a 2X or even a 3X
    Barlow to see if the power will be high enough to split the double.

       Thus, the novice double star observer will be able to predict
    fairly accurately what magnification will be needed if the double
    is in range of the telescope defined.

        For the expert user with acute vision and a superb instrument,
    the program offers the option of calculating the magnification
    required to boost the double to just 2.5 arcminutes apparent
    separation at the eyepiece; the authors and their associates have
    consistently split the famous "Double Double" in Lyra with only about
    60 power, though most books recommend using at least 100 power or
    more.

       After choosing the double star and range needed for its separa-
    tion, the program checks the barrel size and the ocular database,
    employing a standard commercial eyepiece as close to the required
    focal length as possible.  During the search, the program generally
    defers to the widest possible eyepiece apparent fields, although
    these are not necessarily essential for any but the most generously-
    separated "binocular doubles" or naked-eye doubles like Mizar and
    Alcor.

     (2) Get Power

       If the user specifies the power of magnification desired,
    the program will calculate what eyepiece is needed and will select
    one from the ocular database as close as possible to the power
    specified.  The full system performance will then be displayed,
    including any warnings if magnification limits have been exceeded.
    If the eyepiece required is not available (in case the power is
    very low or otherwise out of range) the user may choose other
    options: changing the telescope, barrel size, or adding a Barlow
    to increase the focal ratio.

     (3) Add Barlow

       A Barlow lens may be introduced into the system, and Barlow
    magnification up to nine times is permitted in the case of users
    who wish to stack Barlows for extremely high magnification from


PAGE 10

    short-focal-length guidescopes.  The "GET POWER" function will track
    the inclusion of the Barlow for obtaining magnifications beyond the
    range of standard eyepiece focal lengths.

       If the user wishes to calculate the results of the change in
    effective focal ratio by the inclusion of a magnifying coma corrector
    lens, the magnification factor may be entered by using the Barlow
    function.  Thus, a coma corrector that increases the focal ratio
    by 15% would be entered as a "1.15X Barlow."  Indeed, a Barlow and a coma
    corrector may thus be stacked by specifying their total magnification
    factor: a 2X Barlow and A 1.15 coma corrector would then result in an
    entry of (2) X (1.15) = 2.3 power.

     (4) Other Options Not In Demo Version

       The registered Shareware V/2.5 permits searching the actual database
    values, which are extended even further in Commercial V/3.7x/3.8x to
    over 120 values.  The Commercial editions also provide extremely handy
    functions to specify directly the field of view and exit pupil desired.
    Registered Shareware and Commercial versions permit the printing of
    useful telescope/eyepiece charts.  The Commercial editions have extensive
    instructions on how to best observe solar system/deep sky objects, with
    extra in-depth definition files and lists of resources for developing
    skills in amateur astronomy.  Further details are available in this
    Help menu by reading the file "Upgrade."

     (f) Formulas and Algorithms Employed for Calculations

       This program is intended to be a SEEKER of truth, not an absolute
    arbiter of unalterable facts!  An astronomer should soon learn that
    visual observation is not an absolutely exact science.

       Many formulas for optics and astronomical viewing are, at best,
    only approximations, or are based on subjective experiences.  An
    experienced astronomer with nearly perfect optics may sometimes exceed
    the program's calculations.  If you can do better than this program
    predicts, you may compliment yourself and your equipment!

     (g) A Few Words About the Eyepiece Database and Accuracy of Specs

       In order to aid the user who has only a general idea of the
    different types of eyepiece designs and how their apparent fields
    will affect the ultimate eyepiece view, the authors provide a
    database of eyepieces, representing the GENERAL characteristics of
    oculars that may have been manufactured in the past by several
    different companies.  This database is not intended as a tool to
    recommend the purchase of any type or brand, and cannot possibly
    encompass every eyepiece ever made or sold.  There are over 60
    oculars in the shareware database; the commercial program "SCOPE"
    contains a database with twice as many eyepieces, including the very
    latest long eye-relief types.  If your eyepieces are not in the
    database, the program will permit you to define their focal lengths
    and apparent fields and calculate the system performance.


PAGE 11

       It is difficult to cross-reference and compare with absolute
    precision the types of eyepiece designs of competing manufacturers,
    whose trade-names for specific designs may differ from the classic
    astronomers' definitions of Kellners, Ploessls, Erfles, and so forth.
    Our solution was to set up general guidelines for eyepiece designs
    within certain ranges of apparent fields.  These generic descriptions
    may differ from specific manufacturers' trade names; and different
    manufacturers use diverse methods for measuring the apparent fields,
    so even those data are not precisely comparable.

       Thus, we make no claims that, for example, an "Erfle" of a given
    focal length and apparent field -- though it may be listed in the
    database -- is actually available under that precise description from
    a specific company.  Their version of that "Erfle" may differ in
    number of elements and performance, and may be an enhanced design.
    Use our generic eyepiece-type descriptions, plus the specs for focal
    length and apparent field, to help find a match to the commercial
    eyepiece you wish to purchase.

       The calculations performed by this program are dependent for
    accuracy on the quality of the data input by the user, and the
    correctness of the published specs for telescopes and eyepieces.
    Formulas used for magnification and fields follow the standard methods
    published in any good book on telescope design and performance.  We
    cannot make claims for the accuracy of manufacturers' data, nor do we
    accept responsibility for them.  Our database merely "crunches the
    numbers" that are close to values that may represent real eyepieces.

       Some published optical specifications can be general indicators of
    typical performance in a given model of telescope, rather than precise
    and unvarying values.  In hand-figuring the optics for some telescopes,
    the exact focal length of the system may differ by as much as 15% from
    the nominal value, since surface accuracy, not exact focal length, may be
    the criterion selected in optimizing each unique set of lenses or mirrors.

        Our database has been written with some proprietary techniques that
    take much less disk space and work faster than conventional database
    managers, optimizing the performance of the program on laptops and
    machines with slow CPU clock speed.  Therefore the database structure is
    not editable by the user, but many representative values of focal length
    and field are included.  The commercial program "SCOPE" contains a much
    more complete database, which may be upgraded as new versions of the
    program are prepared.  The commercial version also permits examination
    of the contents of the entire database in order to find desired oculars.

       Most practiced astronomers will agree: the numbers are NOT the most
    important factor in good visual astronomy.  Image sharpness, the flatness
    of the field, efficiency of light transmission, and reliability of the
    performance of an optical product cannot be represented by mere numbers
    describing focal length, apparent field, and so forth.


PAGE 12

     (h) Acknowledgments

       The primary author, Stephen R. Waldee, wishes to thank the highly-
    experienced amateur astronomer Mr. Richard C. Page for his research in
    establishing viewing parameters and testing the criteria used for the
    formulas employed in this program.  Valuable suggestions were made by
    Dr. Douglas Hudgins, Research Scientist, Astrophysics Division, NASA-
    Ames Research Center, Moffet Field, CA., and members of the Tri-Valley
    Star-Stargazers Astronomy Club, Livermore, CA and its president, Alan
    Gorski.

       Invaluable assistance in perfecting details of program construction
    and syntax, and the creation of the eyepiece database algorithms, have
    been provided by co-author Mr. Ron Wood, a gifted astrophotographer and
    computer engineer.  We also appreciate the information about filters
    provided by Dr. Jack Marling of Lumicon, Livermore, California.

     (i) LICENSING INFORMATION AND LIABILITY DISCLAIMER FOR
         WALDEE/WOOD PROGRAM "SHARESCOPE"

       The program SHARESCOPE is offered with no warranty for absolute
    accuracy.  The authors make and you receive no warranties or conditions.
    We do not warrant that this program will operate perfectly on all
    computers, or that it will be free of all error.  We will not be held
    liable for any loss of data, profits, or other direct or indirect damages
    arising from the use of this computer program on your equipment.

        You do not own this copyrighted program, but are permitted to use
    this program for personal and private entertainment and information for
    an evaluation period of 30 days.  If you wish to continue to use
    SHARESCOPE, you must register your copy and receive a license for its
    continued use.  Full information is given in the file reg.doc, which
    may be read from the Help menu by choosing option <r>, "Registration
    Info."

    Copyright (c) February 1993  Stephen R. Waldee  - All Rights Reserved