Int09 version 0.1 (beta)
       By Celso Minnitti Jr. Public domain software. Copy freely.


        INT09_01.ZIP has these files:
        ÉÍÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÍ»
        ³ INT09.ASM     8086 Assembly language source code    ³
        ³ INT09.COM     Executable program                    ³
        ³ INT09.DOC     This document                         ³
        ³ I.BAT         Batch to compile and link INT09.ASM   ³
        ÈÍÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÍ¼


	INT09 is a very simple program designed to explain to everyone how
the Interrupt 9 works. The INT 9 is the Interrupt ReQuest #1 (IRQ1) of the
Intel's 8259 Programmable Interrupt Controller (PIC) that you have in your
PC. So every time one key is pressed AND the bit 1 of I/O port 21h is clear
,set to 0, one int 9 will occur.

	The port 60h will carry the scan code data of the key that has been
pressed. For instance, the key 'A'=1Eh, 'S'=1Fh, 'D'=20h, 'F'=21h, and so on.
Is the BIOS task to translate the scan code data of key 'A' to the Keyboard
Buffer at 40:1Eh.

	That means you will not read the ASCII value 41h for the key 'A'
at the I/O port 60h. Instead it will be 1Eh.

	See the INT09.ASM for more details...


IRQ List
ÄÄÄÄÄÄÄÄ

IRQ0  INT 08	Timer interrupt
IRQ1  INT 09	Keyboard Interrupt
IRQ2  INT 0A	LPT2
IRQ3  INT 0B	Serial Communication (COM2)
IRQ4  INT 0C	Serial Communication (COM1)
IRQ5  INT 0D	Fixed Disk
IRQ6  INT 0E	Diskette controller
IRQ7  INT 0F	Parallel printer


How to contact the Author
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

        If you have any comments or improvement suggestions about INT09
I would like to hear from you. Please call me at 617-235-4018 or write to:

Celso Minnitti Jr
139 Linden St
Wellesley, MA 02181

        And I will be glad to release a more comprehensive, user-friendly,
and much more self explanatory version of INT09 in very single aspect...

	So please feel free to call at any time.


Thanks a lot.

P.S. As you can see this DOC needs a lot of work.