Note: you can load this file into your favorite word processor.





                  ---------------------------------------------------------


                                  PowerSIZE/RES Version 2

                        Residential Load Sizing for HVAC Contractors



                  ----------------------------------------------------------

                                          Contents

                 Section
                    1   PowerSIZE/RES: Introduction
                    2   PowerSIZE/RES: Installation
                    3   PowerSIZE/RES: Tour
                    4   PowerSIZE/RES: Take-Off Tutorial
                    5   PowerSIZE/RES: Design Considerations


                 Appendices


                     Appendix  A
                         License Agreement
                         Disclaimer of Warranty
                     Appendix  B
                         U-Value data
                     Appendix  C
                         Climate data
    



PowerSIZE/RES Computer program and manual copyright (c) 1993 by
D.L.Hughes.  All Rights Reserved. Mailing Address:  Post Office
Box 1671, San Jacinto, CA  92581-1671

Support policy: Due to the technical nature of this program, we
only offer Shareware support by mail at the above address.  Be
sure to include your phone and/or fax number number in all
communications. Be sure to include area code.  CompuServe users may
contact us at 72630,776.









                              1

                PowerSIZE/RES:  Introduction




One of the greatest problems these days for heating and air
contractors is properly sizing equipment.  The reason this is
true is that they have often relied on "rules-of-thumb" to do
residential design work.


"Rules-of-thumb"

But times are changing and the old "rules-of-thumb" are not what
they used to be. Increased insulation, higher performance glazing
products, greater HVAC equipment efficiencies and other factors
are making many of the old rules obsolete.  Dwellings are
becoming more energy efficient and as a result equipment
requirements are not as great.

Too often HVAC contractors are interested in knowing only the
heat loss or heat gain for a dwelling before they make equipment
selection.  These numbers are not adequate to design a system.
In addition to BTU's, designers also need to know CFM's.  The
movement of air is just as important, sometimes more so, than the
heating or cooling capacity of a given piece of equipment.



Science or art?

It's assumed that the person using this program has a background
in HVAC design. Some people like to think that systems design can
be reduced to a pure science, but that's not really the case.
It's an art, too, and experience is an important factor.  This
program will inform your understanding of the thermal dynamics of
a dwelling, but is just one factor in the systems design process.

What else must you know?  It's important that you have a handle
on the range of equipment available, duct layout methods
(including what pressure drops due to air delivery) and
procedures for a good system installation.  The best design in
the world will not help if the system is not properly installed.
In addition there are more mundane things, like the preferences
of the dwelling owner or architect and the amount of money in the
budget.



Verify work

If you use this program and find things that are different from
your experience, it's important that you call program support
line to discuss the matter, or consult with a local mechanical
engineer. Run a few sample jobs to develop an awareness of how
that pro- gram operates, and features that will cause your
numbers to vary widely before relying on the program.  For
example, the cooling BTU's always seem low until someone figures
out that it always comes out "just right" if you drop the summer
inside design temperature down to 74 degrees F.  The only problem
with doing that is that California regulations required that
setting to be left at 78 degrees F!  You need to check to see if
your local jurisdiction has a special interior design temperature
which you are required to use.

Of course this program will be used under a wide variety of
conditions and because of that, you, as the user, are responsible
to make sure values are correct and that the results are applied
in a professional manner.



An Important tool

We think you'll find PowerSIZE/RES a very important tool.  It
will give you the informa- tion you need to size equipment and
design a system.  Based on the  information it provides, you'll
probably be formulating a whole new group of "rules-of-thumb" to
apply to modern, energy-efficient dwellings!


NOTE: Page numbers shown apply to printed manual only.





                                  2
    

                   PowerSIZE/RES:  Installation





In this section we'll learn how to install the program on your
computer.  Then, we'll also install your company name and the
model printer you're using.

Before we get started, make sure your computer meets minimum
systems requirements:

 IBM(tm) or compatible

 DOS version 3.2 or greater.

 A hard-drive with a minimum of a half-megabyte of space
 available.

TIP: you can run this program off a 720k or larger floppy drive,
but it's not recommended because of speed considerations. If you
do want to run it off a floppy be sure that you boot the computer
in such a way that the CONFIG.SYS has the proper number of FILES
and BUFFERS in it.  The program will not run unless these are
properly set a boot-up time.  See below for details.

 Any monitor, color or monographic.

 Any printer.


Are you ready?


Step 1: Create a new hard-drive subdirectory called SIZE (or any
name you desire).

Step 2: Insert either 5.25 or 3.5 distribution diskette in the
appropriate drive (usually A: or B:).

Change the prompt to the appropriate drive (by typing A: or B:,
then <Enter>.  At the proper drive prompt type:

> copy *.* c:\SIZE   (or whatever you named the new subdirectory
you created).

Change back to the SIZE subdirectory, then unzip the program in
the usual way:

> PKUNZIP psrBTU.ZIP



TIP: If you need to set FILES and BUFFERS manually, you may do by
using Copy Con, Edlin, or a text editor to change the CONFIG.SYS
settings.  For details on how Copy Con and Edline work, consult
your DOS manual.  Here are the settings you need: FILES=40
BUFFERS=30

After the installation, you are ready to enter the program by
typing
 
> PSR

at the prompt in the newly created SIZE subdirectory created by
the installation program.



Company/printer installation

Immediately upon typing PSR you find yourself at the "welcome"
screen.  Look it over this first time, then press any key to
continue.

The next screen you see is the "legal" screen.  Please read it,
along with the program license and disclaimer of warranty that
appears in Appendix A of this manual.  Press any key to continue.

After the "legal screen" is the "beg screen".  This is a serious
piece of software, and you are required to register it if you use
it beyond a brief evaluation period (like one job). The
registration fee is only $99.  For this fee you get a complete
manual, the ASHRAE weather data for your state or provience, and,
of course, a copy of PowerSIZE/RES without all the promotional
screens.  You can register your copy of PowerSIZE/RES by sending
your check for $99 to:

D.L.Hughes
Post Office Box 1671
San Jacinto, CA  92581-1671

End of commerical.


Now you find yourself at the MAIN MENU.  Immediately use the
<RightArrow> key (or press the highlighted letter <U> and enter
the Utility option.  The first thing you'll want to do is press
<I> for installation.

Enter all your company data, as much of it will appear on later
reports.

After you exit the last piece of company data, the fax number, a
pop-up scrolling pick window will appear.  You'll be seeing many
of these throughout the program, so we'll take a minute here to
discuss how they all operate.



"Pick" windows

When such a window appears it is filled with data.  You may use
the <UpArrow> or the <DownArrow> to scroll through the data to
find the item you want.  Once you find what you want, press
<Enter> to select (or "pick") the item you can to input.

All such windows have an alternative way of finding things.
Instead of using the arrow keys, you may simply start typing the
letters of the name of the item you're searching for and the
program automatically searches for the item.  For example, the
first printer shown in the selection screen is the Citizen MSP
10, but you want to install an IBM Proprinter XL.  Type the
letters <I> <B> <M> at the top of the selection screen and the
cursor will move directly to the first of two IBM printers
available.  You can then use the arrow key to move you down one
line to the XL model.

If your automatic search is unsuccessful, a tone will sound.
Press <Esc> and start your search again.

TIP:  To overcome bad searches because of typing errors, just
press the first letter in the word you're searching for, such as
<I> in IBM, then use the arrow keys to move to the exact item you
want.

Remember, this search method works on all scrolling pick windows,
such as the climate data window and all the U-value windows.



More about Printers


As you see, in the printer pick window you can select from among
21 different brands and models of printers.  If you have a
printer which is on the list, select it.  If your printer does
not appear, don't worry.  Virtually all dot matrix printers have
an Epson emulation and you should select an Epson model that
works with your printer.  Check your own printer manual for
details.

If you are using a laser printer which is not listed, try the HP
LaserJet II installation. Most laser printers have an HP LaserJet
II emulation.  Again, please check your printer manual for
details about how the emulation works with your printer.

You may need to experiment a bit if your printer is not among the
printers listed. If you have problems, call us and we'll advise
you, perhaps even send you a special printer driver if required.
It has been our experience, however, that special drivers are not
needed because of the Epson/HP LaserJet emulations.

Once you have completed company and printer data, the
installation process is completed.



    


                               3

                       PowerSIZE/RES:  Tour

    
Let's take a quick tour through the program to acquaint you with
the data that goes in each field.  This tour will be of the most
help if PowerSIZE/RES is up and running on your computer screen.

To start the tour, go to the MAIN MENU. If you're still at the
installation screen press <Esc> twice to get there.

TIP:  If you get "lost" in the program you can always press
<Esc>, several times, to get back to the main menu.

If you're just starting the program, press <Enter> twice to get
to the main menu.

We're going to look at each main menu option:



Job file

Use the arrow keys or press <J> to enter the job file.

You now find yourself at the job file menu and you can add or
edit a job.  Press <A> and let's explore how to add a new job.
The job data screen appears and you may input data into the
following fields.  You may not want to actually complete a job
right now, but just "enjoy the sights" as each feature is
explained on this tour.

Owner: Input owner of the job you are sizing.

Job address:  Input the job site address.  If you are unsure,
input parcel number or some other specific identifier so you
won't confuse this job with another one later.

TIP:  The job address is what is known as a "key field".  That
means you will not be allowed to add the same address twice.  If
you try to do so, you'll get an error message.  You can edit any
address as many times as you like, of course, but you can only
add an exact address once.  If you find you must do more than one
calculation at the same address, change the address just a
little.  For example, your first run might be "1234 Oak Street".
Make the second run "1234 Oak Street-2" to avoid conflicts.

City:  City where job is located.

Description: Input a brief description of the job.  Sometimes you
may want to say something like "3 bedroom and den" or you may
want to describe the type of equipment you expect to install,
like "5 ton unit downstairs".  The description is a reference for
your own needs.

Date:  Your computer system date will automatically appear here.
You may change the date if you desire.


Job Data Screen

After exiting the Job Data screen, the program immediately takes
you to the Climate Data/Design Data screen.

TIP: If you want to go back to the Job Data screen, press <PgUp>.
To return back to the Climate/Design screen, press <PgDn>.

IMPORTANT NOTE: In the Shareware version of this program, we have
input one key city for every state in the US and every province
in Canada.  Proper HVAC design dictates that you use the actual
climate data for a site closest to your job.  So, the climate
data provided in the Shareware version is for demonstration
purposes only.  The data is valid, but only if your job is very
near one of the cities listed.  When you register your copy of
PowerSIZE/RES, you'll get more complete ASHRAE climate data for
your state or province.


Location:  You must select a "climate data city location" in
order to do the sizing calculations.  Press <F2> and a scrolling
pick window of locations will appear.  Use the automatic search
function described in the installation section or the <UpArrow>,
<DownArrow> to find the city which is nearest your job site.

Once found, press <Enter> to input the city you have selected.
All the climate data related to that city will automatically
appear on the screen when you select it.

Fields which are automatically filled for you when you select a
city:

Latitude: From ASHRAE data.

Winter Outside Design Temperature: From ASHRAE data.

Summer Outside Design Temperature: From ASHRAE data.

Summer Range: From ASHRAE data.

You must pick a climate data city in all cases.  If you do not
select the city nearest your job site, then all calculations will
not be effective.

TIP:  It's a bad idea to just type in location data into this
screen in a random way. Incorrect data will cause inaccuracies in
your sizing results.  It's always best to "pick" data as
described above.  You can input special weather city data you
want under the "Climate" section of the main menu.  Later, we'll
be discussing that menu option in detail.

Number of bedrooms: This is used to figure the "people load"
which is distributed by the program throughout the dwelling.
Basically the program multiples number of bedrooms x 2 people x
225 BTUH's per person.

Location of ducts:  The default setting is "attic".  If your
ducts are elsewhere, press <F2> and you have the choice of
inputing either "Conditioned" if ducts are in conditioned space
or "mixed" if ducts are in mixed locations such as in attic,
basement or conditioned space.  If most of the ducts are in the
attic, leave it at that setting.

Face velocity: You have the ability to set the velocity of air,
in feet per minute (FPM) that comes from a register.  The default
setting is 500 FPM, and the register make be too noisey if set
higher.  Some designers set the FPM lower, such as 400-450 FPM.


Heating Supply Temp:  This is an important number because it
affects your CFM calculation.  You must input the actual
temperature of the air leaving the furnace.

TIP:  This temperature is sometimes found in product literature,
though you may have to call your supplier and ask.  Of course you
can always stick a thermometer in an existing using to find the
temperature.  Remember, however, that you must measure the
temperature immediately as it leaves the heat source, not any
distance away.

The default heating supply temperature is 130 degrees F, and you
may find that most heating units are very near this figure.  The
more accurate this input is, the more accurate your CFM
calculation will be.

Cooling Supply Temp:  Again, this number affects the accuracy of
your cooling CFM's. Find the temperature in product literature,
by calling your distributor or by using a thermometer on an
existing unit.  The default for temperature is 55 degrees F, and
you may find that most cooling units are very near this figure.

Latent Load Fraction: Set to .20 for dry climates or .30 for
humid climates.

Infiltration: Default set to medium, and this is the best setting
for most dwellings.  The "pick" window pops-up automatically and
you may change this setting to "loose" if it's an old dwelling
and there are strong drafts around windows or doors. You may
change the setting to "tight" if the dwelling is new and special
infiltration barriers have been installed.

Winter Inside Design Temperature:  This is another very important
number.  Some states, like California have set inside design
temperature by law.  It is 70 degrees F in California and needs
to be left at that figure.  This is a good number to use, though
you may want to check to see if your state has another
requirement.

Summer Inside Design Temperature: Again, this is a very important
number.  In California the default is 78 degrees F and needs to
be left at the number in that state.  If you are using this
program in a state other than California, check the regulations
for a different requirement. In the HVAC industry the 78 degree
inside design temperature is not popular since hardly anyone sets
their thermostat that high and equipment may be undersized on a
BTUH basis alone.  Many industry people prefer a 74 degree summer
inside design temperature and that is a good number to use unless
regulations do not allow it.


After entering the last item, the program automatically takes you
to the Room Data Menu.


TIP:  When at the design data screen you press <F2> to select the
climate city location. Then go down and add the number of
bedrooms by either pressing the <Enter> or <DownArrow> key four
times.  If you're satisfied with all the other default inputs
after inputing the number of bedrooms, just press <PgDn> at that
point and you'll automatically come to the Room Data Menu.


Room/Zone Data


Now, at the Room Data Menu, press <A> to add room data.


Individual Room/Zone: Input the name of the room you want to
size.  Instead of a specific room, you may want to input the name
of a zone.  Both methods are explained in the tutorial section of
this manual.

TIP:  You may occasionally want to do sizing for a whole house.
It's easy to do.  Just input HOUSE in the room/zone field and
input whole house totals into the various fields that follow.
 

Conditioned Floor Area:  The CFA is another important number.  It
is the square footage of the actual space being heated and/or
cooled.  Sometimes a set of plans will show a gross square
footage which includes garage, porches and patios.  This is not
the number that is important to you.  You want only the net area
that is being heated or cooled, the area known as the
"conditioned floor area".

Average Ceiling Height:  The height, in lineal feet, from floor
to ceiling.  For cathedral ceilings take the high and low and
average the two.

Slab perimeter:  There are two components to the slab perimeter.
Of course if you are dealing with a house that has only a raised
floor, you can skip these inputs.  The two components for slabs
are length, in lineal feet, and the actual F2-factor. Key:
F2factor1 = Hard surface in rooms along perimeter of dwelling.
F2factor2 = Covered surface (carpet, cupboards, etc) along
perimeter. F2factor3 = Perimeter of house touches garage, porch,
patio, covered F2factor4 = Perimeter of house touches garage,
proch, patio, exposed

Input the perimeter of each type in lineal feet.  If there is no
slabedge insulation used, then leave the F2 factors at the
default shown.  If slabedge insulation is being used, then
consult the chart in Appendix B and use the appropriate number
from it. Note: these charts don't appear well on a computer
screen.  You're going to need to register your program to get the
printed manual where Appendix B appears.

Roof/Ceiling SF: Square footage of roof/ceiling assembly of
room/zone goes in first field. This is commonly the square
footage of the house in a single story dwelling.  You may have to
measure from plans in multiple story dwellings.  The U-value of
the roof/ceiling assembly goes in the second field.  Press <F2>
to pop-up a selection of assemblies from which to select.  If you
do not find a match, consult Appendix B.

Raised Floor SF:  Square Footage of raised floor in this
room/zone if any.  Remember this area counts only if one side of
the floor is in conditioned space and the other side is in
unconditioned (ambient) space.  Do not count area of floors where
the space is conditioned on both side of the floor, such as is
common in two story houses.  The second input is for the floor
U-value.  Press <F2> to select from scrolling pick window.
Consult Appendix B if you cannot find the assembly you need in
the pick window.

Skylights:  There are three parts to the skylight input.  First
is the area of skylights in the zone in square feet; second, the
U-value (press <F2> for selection); third, the shading
coefficient of the skylight <again, press <F2> for selection).
If you do not know if the skylight has shading leave the default
number at the 1.00 shown on the screen.

Number of Appliances:  Used to figure appliance heat gain in this
room/zone.  Include all major appliance is the zone.  Be sure to
count range and oven as separate appliances even if they are one
unit.  Count dishwasher, washer and dryer, refrigerator and
freezer if in conditioned floor area.  Ignore small appliances
like garbage disposals, toasters, etc.

Now we come to the vertical surfaces section for this zone.

The cursor automatically moves into this area, and you must press
<RightArrow> to pop-up the orientation pick window. When the
window appears, select the orientation by moving the light bar to
the desired azimuth and pressing <Enter>.  You may correct an
entry by pressing the <UpArrow> and making another selection.
Note: do not just type in an orientation.  Always use the pick
window to select.


Wall Square Footage:  Input area of net wall of room/zone for
this orientation.

Wall U-value:  Press <F2> to select wall U-values.  If you cannot
find a value to match the walls shown on the plans, consult
Appendix B.

Fenestration (Glazing) Square Footage: Input area of glass of
room/zone for this orientation.

Fenestration U-value: Press <F2> to make selection.

Fenestration shading coefficients:  If window has a shading
device, like drapes or blinds, press <F2> and make selection.

TIP:  Including shading coefficients will severely reduce cooling
load.  If you are unsure of the shading devices that will be
used, or that owners will open and close them at the proper time
each day, or if you think the window coverings might be changed
by new owners at a later time, it is best to leave the shading
coefficient at the 1.00 default.

You have just completed a room/zone and are back at the Room Data
menu.  If you want to add another room/zone to this dwelling
address, press <A> to add.  Repeat this process for each
room/zone.

TIP:  Repeating this process is not as tiresome as it may seem.
The U-values you input for this house are retained, so all you
have to do is change those U-values that apply.  Of course you
must input measurements for each room/zone, but that data is
quickly available from your take-off sheet as explained in the
tutorial section.
 
If you need to edit any room/zone in this dwelling, press <E> at
the Room Data Menu. If you have finished all inputs, press <Esc>
to return to the Job File Menu.

If you want to edit a job file, press <E> and you'll find
yourself at a scrolling pick window which shows job address and
description. Move to the job you want, then press <Enter> to
select.  Note: This edit selection screen is the only place in
the entire program where you can delete a job.  To do so, move
the lightbar to the job you want to delete, then press the <Del>
key.  Be careful, the deletion is permanent!

When you are in edit mode you can move through the screens in the
same way as described for the "add" mode described above.  If you
get "lost" you can always press the <Esc> key repeatedly until
you get back to the Main Menu.



                                    Back at the Main Menu


We've just gone through the process of inputing dwelling data for
sizing.  The next thing that you may logically want to do is
print the sizing report.  To do so, press <R> at the Main Menu.


Report Option

NOTE:  There may be a difference in totals between the Room-by-Room
report and the Heating and/or Cooling reports.  This is because two
different menthods are used to arrive at the same numbers.  Also, the
rounding of numbers has a slight influence.  If totals are off
more than a few hundred BTUH's, go back to room-by-room menu and move
the cursor through the entire screen of one room of the dwelling.  This
process serves to "force" calculations, and the totals of the two kinds of
reports should be very similar.

Upon pressing <R>, another pick window appears, and you select
the job you want to print by address.  Press <Enter> to select
the highlighted address and another menu appears.  You may send
the report to either the screen or the printer.  Make your
selection, then wait a few moments while the report is processed.



Climate Option

The climate data is in a separate database which is accessed by
pressing <C> at the Main Menu.

Here you see all the design information which is needed to size a
dwelling.  Happily, you can ignore all this if you desire because
the relevant information is automatically input into the
PowerSIZE/RES when you select the climate location city.

*** NOTE: The following options ares not available in the
Shareware version.  In the Shareware version you are limited to
the selected cities, one for each state and province. When you
register your copy of PowerSIZE/RES you will receive more
complete climate data for your state or provience.

However, you may want to add, edit or delete climate information,
and this is the spot to do it.

ADD: To add information, press the <Ins> key.  Be sure you have
ALL the information you need when adding a climate location.
This information is available from ASHRAE or other sources.
WARNING: if you input wrong or incomplete information here, you
will get wrong or incomplete load sizing calculations!


EDIT:  To edit information, highlight the line you want to
change, then press the <RightArrow>.  Move the cursor to the item
you want to change and change it.  Press <Enter> as many times as
you need to get to the end of the line.  The change will be
automatically saved.  WARNING: Be sure you are making the change
for valid reasons. Wrong or incomplete information will result in
wrong or incomplete load sizing!


DELETE:  To delete a climate location, highlight the city then
press the <Del> key. This will permanently delete the highlighted
city.  NOTE: Sometimes people think they are saving disk space by
deleting cities they don't use.  Usually this is false economy as
it is very desirable to have all the locations instantly
available when you want them.  It's a better idea not to delete
any climate locations in the database. To leave the climate
location database, press <Esc> and you'll be back at the Main
Menu.



Utility Option

If you read the installation section of this manual, you have
already had a brief look at the utility option.  If you have not
done the company and printer installation, please go back and
read section 2 now as we won't repeat that data here.

NOTE: "File maintenance" is a "cure-all" for most data problems.
Please read the next paragraph carefully!

File maintenance: The file maintenance option automates the
purging and reindexing of program files.  If you are using the
program heavily, do a file maintenance weekly.  You will also
want to use this option if your data files get "corrupted" for
any reason, like a power loss.  In fact, file maintenance is kind
of a "cure all".  If you experience any problems with "lost"
data, failure to print, etc. do a file maintenance and you'll
probably find that every thing has been set right.  To do a file
maintenance, just press <F> and the program does all the work.

DOS Services:  In the PowerSIZE/RES program and need to run
another program or use some DOS command?  All you have to do is
press <D> and you find yourself at a DOS prompt.  Go ahead and do
what you need to do.  After exiting the other program, or
executing a DOS command, type EXIT and you're back in
PowerSIZE/RES.
  
Now back to the Main Menu.


Quit Option

Always quit PowerSIZE/RES in an orderly way.  That is, don't shut
off the machine in the middle of a session, but instead go to the
main menu and press the <Q> key.  By doing so you'll close out
the program in the proper way and get a nice final message on the
screen telling you the exit was normal.

If you don't see the message it means the exit was not normal.
In that case run the program again and IMMEDIATELY go to the file
maintenance option in the utility menu.  This will restore data
that might have been lost by a disorderly exit.


Well, that's the end of your guided tour.  Hope you enjoyed the
trip!


 
                                    Data Backup Procudure

It's important that you backup your data files often as insurance
against data loss.

To backup your files use the DOS "COPY" or "BACKUP" commands to
archive the all files with *.DBF and *.NTX extensions.  An
example using the "COPY" command:

C:\> Copy *.DBF A:

wait until files have been copied from C: to A:

C:\> Copy *.NTX A:

wait until files have been copied from C: to A: Backup complete.

If you have questions about the DOS "COPY" or "BACKUP" commands,
please consult your DOS manual.


    




                                    4

               PowerSIZE/RES:  Take-Off Tutorial




In this section we'll discuss the procedure for doing a sizing
calculation.  We will focus on how to collect the data from the
plans to put into the program.

Once the data has been collected, then you can input it into
PowerSIZE/RES is the manner described in the previous section.

Your objective is to take a set of plans and collect data from
them in a fast and accurate manner.  To help you achieve this
goal there is a special plan take-off sheet at the end of this
chapter for you to photocopy and use.  We'll use this sheet and
the sample plan on the following pages to an actual take-off.

IMPORTANT NOTE:  As we do this take-off, we are only interested
in surfaces (walls, roofs, floors, etc.) where it is conditioned
space on one side and unconditioned (ambient) space of the other
side.  Your load calculations will be inaccurate if you include
any surfaces which are either conditioned on both sides or
ambient on both sides.


One Step at a Time


Step 1: Input "general data".  All of this data is
self-explanatory, except perhaps for the heating/cooling supply
temperatures.  These temperatures are discussed fully on page 11
of this manual.


Step 2: View the plans and see how your going to divide up the
rooms.  Note page 21 to see how we have done this.  Normally you
will want to do your take-off on a strictly


*** NOTE:  We provide you with special take-off forms to make the
job easier.  This take-off form is described below.  However, the
form does not reproduce well on the the screen.  You will receive
a copy of the special take-off form in your printed manual when
you register your copy of PowerSIZE/RES

Room-by-room basis, but there are times when you'll group areas
together.  For example, on page 21 we have lumped the kitchen and
family room together into Room 1 since it is one big space.  It's
true you'll only get one BTU and CFM load for this area, but it
will be easy to split the totals when you do your layout.

Another case of combining areas is Room 6, where bedroom 2 and
hall area are grouped together.  We need to account for all the
conditioned floor area in a dwelling, so sometimes it's helpful
to group areas like this, especially in a small house like our
example.  If you were dealing with a huge house where hall areas
might have their own registers, then grouping would not be
helpful.


TIP: Total the CFA (Conditioned floor area) on your take-off
sheet to make sure that it matches the figure shown on the plans.
It's easy to miss some portion of the dwelling, and when you do
your load calculations will not be accurate.  A simple comparison
of numbers will solve the problem.


Step 3:  Once you have decided how you're going to divide-up the
dwelling, list the Room # and the Room name on the take-off
sheet.  Then go systematically around the dwelling and write the
compass orientation.  That is, what direction a particular wall
is facing.  Notice our example, there is only one room (#7) that
faces a single direction. All the rest are corner rooms and face
2 different directions.


TIP:  You have a choice here.  One choice is to write down data
as we have here using a "/" mark to differentiate between the
various areas that apply to different orientation.  That is, we
have shown there is a gross wall area of 176 SF facing south, and
120 SF facing east. This is a quick and easy way to gather the
data when a house is small.  However, when a house is large, you
may want to have a separate line for each orientation.  An
example:

         Room      Facing Room #   Name      NSEW

1        Kit/Fam     S 1a       Kit/Fam     E    .... and so
forth.

This method makes complex projects clearer, and is just as easy
to use when you input data into PowerSIZE/RES.


Step 4:  Next determine the square footage of each room or
grouping and write it in the appropriate space.


Step 5:  Determine the ceiling height of each room.  Most rooms
are eight feet tall, but you should consult the section plan (see
page 20) to see if some ceilings are higher. Note that in the
case of our example the living room is the only room that has a
ceiling higher than eight feet.  It is eight feet on the low side
and twelve on the high side, so we're going to call this average
ceiling height ten feet.


Step 6:  Next is the slab perimeter data.  On the take-off form
we have written down 22 lineal feet of exposed slabedge in the
Kit/Fam area, and since there is no slabedge insulation in this
house we have put a "D" down for "default", the value already
input into PowerSIZE/RES.  If slabedge insulation is used on your
job, consult the last page of Appendix B for the correct value.
You would write down that value instead of a "D".

The Kit/Fam area also has 15 lineal feet of covered slabedge, the
length of wall covered by cabinets.   The example shows all the
other perimeter is covered by carpet.  Even though the living
room is covered by carpet, we applied 22 feet of its length to
SP3 because it adjoins the garage.


Step 7:  Roof areas in a single story house match the room area.
We just wrote "R-30" as a notation for ceiling insulation and
will select the exact value from the "pick" window when we input
the data into PowerSIZE/RES.
 

Step 8:  In our example, there is no raised floor so we have left
these columns blank.  In most cases the area would be the same as
the CFA.


TIP: One of the places where raised floors are commonly missed is
the slab-floor house which has a room over the garage.  Since the
garage is ambient space (if it has no registers), the floor above
is "raised".


Step 9:  Skylight square footage, U-value and shading
coefficient.  Our sample house has no skylights, but if it did
we'd include the appropriate values in the three spaces allowed.
If your project has skylights, remember to subtract their total
square footage from the roof total for the room.


Step 10:  Number of appliances.  Input the number of major
appliances found in the room.

TIP: PowerSIZE/RES automatically distributes heat gain from
people to rooms throughout the dwelling.  However, the heat gain
from appliances stays with the room where you input them.  If you
want to distribute appliance gain to other rooms, just input a
number in the room where you want the gain to show.  Never input
more appliances in rooms than the house actually contains.


Step 11:  Input room wall square footage (length x height) on the
appropriate line.  Be sure to subtract fenestration area to get
net wall area.  Yes, this is in reverse order on the form, but we
wanted the form laid out in such a way that it would be easy to
use data from it to input into PowerSIZE/RES.   Sorry, we just
couldn't have it both ways!

Write down the wall U-value as it appears on the plans, then pick
the exact value from the "pick" window when you input it into
PowerSIZE/RES.  By the way, give the section plan a good look as
sometimes the wall insulation value changes from wall-to-wall.


Step 12:  Next, write down fenestration (glazing) totals, along
with the U-value of the glass.  Fenestration shading, such as
drapes or blinds, cause special concerns for HVAC contractors
since the devices are often not open and closed at proper times
by homeowners.  We have shown no interior shading devices in our
example.  See page 14 of this manual for a more complete
discussion of whether or not interior shading devices should be
added to a dwelling for sizing purposes.


That's it!  Now you are ready to input this information into
PowerSIZE/RES!






                                                 5

                               PowerSIZE/RES: Design
                               Considerations



PowerSIZE/RES calculates BTUH's and CFM's for each room, and
provides the free space required, in square inches, for registers
in each room.  Once you have this information in hand, it's easy
to design a system.

The program makes a number of assumptions, and we'll cover some
of them here, and also give some tips for good design.


Ducts and Registers

  It's assumed that the room you have input will have a register,
and optionally a return air grille.  If a space does not have a
supply, then you'll want to combine it with a room that does.

  Return air grilles should be one size larger than the supply
register.  If you have a central return air, be sure to that all
doors are undercut so air will flow freely back to the source.

  Anytime PowerSIZE/RES calculates a room as having less than 50
CFM, the lower number is over-ridden and 50 becomes the minimum.
The 50 CFM minimum is important because air will become stale if
it's not moving at least at this volume.  This is particularly
important for bathrooms.  You may want to adjust CFM's in other
rooms as well.
  
  You must evaluate total CFM because the total of man CFM
minimums may mean larger ducts as well as throwing you into the
next largest equipment size.  This may be counterproductive from
a cost standpoint, so you may want to use the small equipment an
scrimp a bit on CFM's in areas where impact will be small.

   If heat loss exceeds 10,000 BTUH in a given room, use more
than one supply.  Do this also in rooms with large non-north
facing windows.

   PowerSIZE/RES computes register free space based upon a face
velocity of 500 FPM.  You can use this number as a guide when
selecting registers, as free space is one of the selection
criteria which appears on most product specification sheets.
There are other considerations when selecting registers: pressure
loss (normally 0.1 Inches of Water for duct run of less than 100
feet, 0.05 for runs greater than 100 feet.) and "throw".  The
horizontal throw of air should ideally be 3/4 the distance across
the room from the register.
     
   To reduce drafts in smaller rooms, increase register to the
   next larger size.

   Once PowerSIZE/RES provides you with CFM's by room, use an Air
Duct Calculator (provided free by most HVAC equipment
manufacturers) or chart (see next page) to determine duct size.
Select "Friction per 100 Feet of Duct" (0.1 for most residences)
and match it with the CFM for the specific room.  Then, note the
"Round Duct Diameter".  For example, if the Friction is 0.1, the
CFM is 100, the round duct size would be 6 inches in diameter.
Use the chart on page 29 to translate round duct diameter to
rectangular ducts, if needed.  Note: Chart not available in
Shareware version.

    When sizing a duct system, always start at the supply
register which is the greatest distance from the HVAC unit, then
work back to the unit.  This duct will remain the same size until
it joins a larger duct.  That duct will increase in size based
upon how many smaller ducts join it.  If there any chance that
cooling will be installed, always size ducts to accomodate it.


Heating/ Cooling Equipment Selection


   Equipment efficiency is of growing importance in these days of
ever-increasing energy costs.  The higher the efficiency (AFUE
for heating, SEER for cooling), the less energy costs will be for
homeowners.  Everyone today ought to be selling the highest
efficiency equipment possible.  The only problem with this is
that high efficiency equipment is more costly, and the job will
probably go to the contractor who bids cheap, minimum efficient
equipment.  Wise contractor's will sell the benefits of high
efficiency equipment to their clients, as "value" is more
important that "cost".
 
   When selecting a furnace remember that peak OUTPUT of the unit
should never be less than the heat loss of the building.  But
BTUH's are just one part of the issue; also be sure the furnace
has adequate CFM's.

   Along with CFM's you must consider pressure drops to determine
if you have adequate fan volume.  The static pressure of the unit
fan must equal or exceed the system pressure drops.  How do you
figure pressure drops in a system?  Here are some typical
numbers:

             Return air inlet        0.05
             Filter when dirty       0.10
             Cooling coil            0.20
             Supply outlet           0.05
             Duct pressure drop      0.10*

                          Total      0.50       

This means the furnace you select must be able to provide at
least the total CFM shown by PowerSIZE/RES at this total external
static pressure, though you'll probably want to select the next
size up rather than depend on the unit working properly at it's
minimum performance standard.  Note: If computed external static
pressure is not shown in furnace product literature, select the
next larger pressure shown.

If the CFM is too high at the required external static pressure
(causing noise and excessive drafts), install a damper and adjust
it to the proper CFM.

* To figure the exact duct pressure drop use this equation:

Inches of Water = Length of longest run (lineal feet) x 1.5 x  .1
/ 100

Example:   82 x 1.5 x .1 / 100 = 0.123 Inches of Water


   Today, selecting an appropriate cooling unit (coil/condenser)
is much easier than in the past because manufacturers are making
companion units.  That is, a certain heating unit requires a
matching cooling unit.

   If your job has cooling, be sure the coil CFM (at the correct
pressure drop) requirements and the volume of air available are a
match.


Always keep in mind that the configuration of the dwelling,
climate conditions, local regulations, the performance of
equipment from differing manufacturers and other elements can
affect system design and selection.  You are advised to consult
with general contractor, mechanical engineer, local building
officials, HVAC equipment distributor or any other required
professional before committing yourself to any specific design.








                                Appendix A



                                 License and
                            Disclaimer of Warranty




                             License Agreement


Shareware version

Any vendor or individual is granted the right to distribute this copyrighted
Shareware version 1.A of PowerSIZE/RES as long as:

1) The complete program is included on all distribution disks.
2) Notice is provided that this is the Shareware version, and that if
the program is used beyond a brief evaluation period, registration and
payment of $99 fee is expected.



Registered version

This is a single copy software license granted by D.L.Hughes,
Post Office Box 1671, San Jacinto, CA 92581-1671.  The software
is licensed to you as the end user.  It is not sold.  You are
granted a nontransferable and nonexclusive license to the
original purchaser of PowerSIZE/RES  This program must be used
only on a single computer. Archival copies may be made by the
purchaser, but Federal law provides severe penalties for the
unauthorized reproduction, distribution or exploitation of
copyrighted computer programs.

Disclaimer of Warranty. This program is sold without any express
or implied warranty. Because of the diversity of conditions and
hardware under which the program may be used, no warranty of
fitness for a particular purpose is offered.  The user is advised
to test the program thoroughly before relying on it.  The user
must assume the entire risk of using the program.  Any liability
of seller or manufacturer will be limited exclusively to product
replacement or refund of the purchase price.





                             Appendix B


              U-values of construction assemblies

NOTE: These charts are not avaiable in the Shareware version.



                             Appendix C

                            Climate data

Note: These charts are not available in the Shareware version.