FrontDoor 2.11 Shareware

        User guide

        For noncommercial use and distribution































                To the memories of Catharina Frodin and Alva Gardlund.
                   And to Christian, Katja, and Igor Homrighausen.

                             Party on Fred, we miss you.




        Table of contents

        1 SHAREWARE VERSION LICENCE AGREEMENT - "FFHA184k"  . . . . . . .   1

        2 Preface . . . . . . . . . . . . . . . . . . . . . . . . . . . .   3
            2.1 Hardware requirements . . . . . . . . . . . . . . . . . .   3
            2.2 Software requirements . . . . . . . . . . . . . . . . . .   3
            2.3 Additional equipment  . . . . . . . . . . . . . . . . . .   3
            2.4 BBS software  . . . . . . . . . . . . . . . . . . . . . .   4

        3 Installation  . . . . . . . . . . . . . . . . . . . . . . . . .   4
            3.1 CONFIG.SYS  . . . . . . . . . . . . . . . . . . . . . . .   4
            3.2 AUTOEXEC.BAT  . . . . . . . . . . . . . . . . . . . . . .   4
            3.3 Directories . . . . . . . . . . . . . . . . . . . . . . .   4
            3.4 Files . . . . . . . . . . . . . . . . . . . . . . . . . .   4

        4 Setup . . . . . . . . . . . . . . . . . . . . . . . . . . . . .   5
            4.1 FD environment variable . . . . . . . . . . . . . . . . .   5
            4.2 FD.SYS <> SETUP.FD  . . . . . . . . . . . . . . . . . . .   5
            4.3 Getting started . . . . . . . . . . . . . . . . . . . . .   5
            4.4 Menus . . . . . . . . . . . . . . . . . . . . . . . . . .   6
                4.4.1 File  . . . . . . . . . . . . . . . . . . . . . . .   6
                4.4.2 Global  . . . . . . . . . . . . . . . . . . . . . .   6
                4.4.4 Editor  . . . . . . . . . . . . . . . . . . . . .    17
                4.4.5 Terminal  . . . . . . . . . . . . . . . . . . . .    20
                4.4.6 Modem . . . . . . . . . . . . . . . . . . . . . .    24
                4.4.7 Printer . . . . . . . . . . . . . . . . . . . . .    24
                4.4.8 Manager . . . . . . . . . . . . . . . . . . . . .    24
                Event Manager . . . . . . . . . . . . . . . . . . . . .    24
                Folder Manager  . . . . . . . . . . . . . . . . . . . .    24
                Security  . . . . . . . . . . . . . . . . . . . . . . .    27
                    Notes regarding protocols . . . . . . . . . . . . .    28
                    Request Manager . . . . . . . . . . . . . . . . . .    29

        5 The nodelist and the nodelist compiler  . . . . . . . . . . .    29
            Zone  . . . . . . . . . . . . . . . . . . . . . . . . . . .    29
            Region  . . . . . . . . . . . . . . . . . . . . . . . . . .    29
            Net . . . . . . . . . . . . . . . . . . . . . . . . . . . .    29
            Node  . . . . . . . . . . . . . . . . . . . . . . . . . . .    29
            Point . . . . . . . . . . . . . . . . . . . . . . . . . . .    30
            5.1 Hosts and hubs  . . . . . . . . . . . . . . . . . . . .    30
            5.2 Compiling a nodelist  . . . . . . . . . . . . . . . . .    30
                5.2.1 FDNODE.CTL  . . . . . . . . . . . . . . . . . . .    30
                    POINTLIST . . . . . . . . . . . . . . . . . . . . .    30
                    PVTLIST . . . . . . . . . . . . . . . . . . . . . .    31
                    SWEPULSE  . . . . . . . . . . . . . . . . . . . . .    32
                    PHONE . . . . . . . . . . . . . . . . . . . . . . .    32
                    USE ZONE  . . . . . . . . . . . . . . . . . . . . .    32
                    DIAL  . . . . . . . . . . . . . . . . . . . . . . .    32
                    COST  . . . . . . . . . . . . . . . . . . . . . . .    34
            5.3 Nodelist flags  . . . . . . . . . . . . . . . . . . . .    34
            5.4 Command line switches . . . . . . . . . . . . . . . . .    34
            5.5 Points  . . . . . . . . . . . . . . . . . . . . . . . .    35
                5.5.1 Pointlist . . . . . . . . . . . . . . . . . . . .    35
                5.5.2 FDNODE.CTL  . . . . . . . . . . . . . . . . . . .    36
                5.5.3 Treatment of points . . . . . . . . . . . . . . .    37
                5.5.4 Remapping . . . . . . . . . . . . . . . . . . . .    37
                5.5.5 POINTNET  . . . . . . . . . . . . . . . . . . . .    37
            5.6 Sharing the nodelist  . . . . . . . . . . . . . . . . .    38




        6 Modems and FOSSIL drivers . . . . . . . . . . . . . . . . . .    38
            6.1 Basic configuration . . . . . . . . . . . . . . . . . .    38
                Hardware  . . . . . . . . . . . . . . . . . . . . . . .    38
                    Serial port . . . . . . . . . . . . . . . . . . . .    39
                    Locked port . . . . . . . . . . . . . . . . . . . .    39
                    Maximum baudrate  . . . . . . . . . . . . . . . . .    39
                    Reset modem to connect speed  . . . . . . . . . . .    39
                    Lower DTR when busy . . . . . . . . . . . . . . . .    39
                    Lower DTR to terminate call . . . . . . . . . . . .    39
                    Toggle DTR before dialing . . . . . . . . . . . . .    39
                    Carrier detect mask (CDMASK)  . . . . . . . . . . .    40
                Connect messages  . . . . . . . . . . . . . . . . . . .    40
                Status messages . . . . . . . . . . . . . . . . . . . .    40
                Custom message  . . . . . . . . . . . . . . . . . . . .    40
                Command strings . . . . . . . . . . . . . . . . . . . .    40
                    Escape code . . . . . . . . . . . . . . . . . . . .    40
                    Return on-line  . . . . . . . . . . . . . . . . . .    40
                    Onhook  . . . . . . . . . . . . . . . . . . . . . .    40
                    Offhook . . . . . . . . . . . . . . . . . . . . . .    41
                    Dial  . . . . . . . . . . . . . . . . . . . . . . .    41
                    Suffix  . . . . . . . . . . . . . . . . . . . . . .    41
                    Delay . . . . . . . . . . . . . . . . . . . . . . .    41
                    Init-1..Init-3  . . . . . . . . . . . . . . . . . .    41
                    Down  . . . . . . . . . . . . . . . . . . . . . . .    41
                    Reset . . . . . . . . . . . . . . . . . . . . . . .    41
                Answer control  . . . . . . . . . . . . . . . . . . . .    42
                    Manual answer . . . . . . . . . . . . . . . . . . .    42
                Fax . . . . . . . . . . . . . . . . . . . . . . . . . .    42
            6.2 Advanced configuration  . . . . . . . . . . . . . . . .    42
                6.3 The Modem Manager . . . . . . . . . . . . . . . . .    43
                An example, the HST/DS  . . . . . . . . . . . . . . . .    43
            6.4 FOSSIL drivers  . . . . . . . . . . . . . . . . . . . .    44
                BNU . . . . . . . . . . . . . . . . . . . . . . . . . .    44
                X00 . . . . . . . . . . . . . . . . . . . . . . . . . .    45
                OS/2 2.x  . . . . . . . . . . . . . . . . . . . . . . .    45

        7 Events  . . . . . . . . . . . . . . . . . . . . . . . . . . .    46
            7.1 The Event Manager . . . . . . . . . . . . . . . . . . .    46
                7.1.1 External event behavior . . . . . . . . . . . . .    48
                7.1.2 Mail event behavior . . . . . . . . . . . . . . .    48
                7.1.3 The @ event . . . . . . . . . . . . . . . . . . .    50
                7.1.4 Overlapping events  . . . . . . . . . . . . . . .    51

        8 Mailer  . . . . . . . . . . . . . . . . . . . . . . . . . . .    51
            8.1 Menus . . . . . . . . . . . . . . . . . . . . . . . . .    51
                8.1.1 Programs      <Alt-P> . . . . . . . . . . . . . .    51
                8.1.2 Utilities     <Alt-U> . . . . . . . . . . . . . .    52
                8.1.3 Mail          <Alt-M> . . . . . . . . . . . . . .    53
                8.1.4 Your profile  . . . . . . . . . . . . . . . . . .    54
            8.2 Mail queue      <Alt-B> . . . . . . . . . . . . . . . .    54
            8.3 Call progress . . . . . . . . . . . . . . . . . . . . .    56
            8.4 Semaphore indicators  . . . . . . . . . . . . . . . . .    56
            8.5 Undialable  . . . . . . . . . . . . . . . . . . . . . .    56

        9 Editor  . . . . . . . . . . . . . . . . . . . . . . . . . . .    56
            9.1 Main            <Alt-M> . . . . . . . . . . . . . . . .    57
            9.2 Edit            <Alt-E> . . . . . . . . . . . . . . . .    58
                9.2.1 Edit mode <Alt-T> . . . . . . . . . . . . . . . .    59
                9.2.2 Toggle    <Ctrl-F2> . . . . . . . . . . . . . . .    60




            9.3 Utilities       <Alt-U> . . . . . . . . . . . . . . . .    60
            9.4 Purge           <Alt-P> . . . . . . . . . . . . . . . .    62
            9.6 Entering new messages . . . . . . . . . . . . . . . . .    63
            9.7 Message survey  <Alt-F9>  . . . . . . . . . . . . . . .    63
                9.7.1 Main menu . . . . . . . . . . . . . . . . . . . .    63
                9.7.2 Continuous tagging  . . . . . . . . . . . . . . .    64
                9.7.3 Range select  <F4>  . . . . . . . . . . . . . . .    64
            9.8 Keyboard macros . . . . . . . . . . . . . . . . . . . .    65
                Examples  . . . . . . . . . . . . . . . . . . . . . . .    66
            9.9 Carbon copies (CC)  . . . . . . . . . . . . . . . . . .    66
                9.9.1 Hidden CCs  . . . . . . . . . . . . . . . . . . .    67
                9.9.2 Using files as input to CCs . . . . . . . . . . .    67
                9.9.3 Address expansion . . . . . . . . . . . . . . . .    67
            9.10 Blind Carbon Copies (BCC)  . . . . . . . . . . . . . .    67
            9.11 Crossposting (XC)  . . . . . . . . . . . . . . . . . .    68

        10 Terminal . . . . . . . . . . . . . . . . . . . . . . . . . .    68
            10.1 Menus  . . . . . . . . . . . . . . . . . . . . . . . .    69
                10.1.1 File         <Alt-F> . . . . . . . . . . . . . .    69
                10.1.2 Line settings    <Alt-L> . . . . . . . . . . . .    70
                10.1.3 Session      <Alt-S> . . . . . . . . . . . . . .    71
                10.1.4 Options      <Alt-O> . . . . . . . . . . . . . .    73
            10.2 Keyboard macros  . . . . . . . . . . . . . . . . . . .    73
            10.3 Raw mode . . . . . . . . . . . . . . . . . . . . . . .    73
            10.4 Keypad modes . . . . . . . . . . . . . . . . . . . . .    74
            10.5 PC keyboards . . . . . . . . . . . . . . . . . . . . .    74
            10.6 Phone directory    <Alt-P> . . . . . . . . . . . . . .    74
                10.6.1 Queue status . . . . . . . . . . . . . . . . . .    75
                10.6.2 Adding/changing entries  . . . . . . . . . . . .    75
            10.7 Inactivity timer . . . . . . . . . . . . . . . . . . .    75
            10.8 File transfers . . . . . . . . . . . . . . . . . . . .    76
            10.9 On-line timer  . . . . . . . . . . . . . . . . . . . .    76

        11 Miscellaneous  . . . . . . . . . . . . . . . . . . . . . . .    76
            11.1 Destination of messages  . . . . . . . . . . . . . . .    76
                11.1.1 Name lookups . . . . . . . . . . . . . . . . . .    76
                11.1.2 Address browsing . . . . . . . . . . . . . . . .    76
                11.1.3 Address macros (NAMES.FD)  . . . . . . . . . . .    77

        12 File Requests  . . . . . . . . . . . . . . . . . . . . . . .    78
            12.1 Outbound Requests  . . . . . . . . . . . . . . . . . .    78
            12.2 Requesting files with a password . . . . . . . . . . .    79
            12.3 Update Requests  . . . . . . . . . . . . . . . . . . .    79
            12.4 Inbound Requests . . . . . . . . . . . . . . . . . . .    79
                12.4.1 Request modes  . . . . . . . . . . . . . . . . .    79
                    Anyone can request  . . . . . . . . . . . . . . . .    79
                    Systems in nodelist can request . . . . . . . . . .    79
                    No requests . . . . . . . . . . . . . . . . . . . .    79
                12.4.2 Directory listings . . . . . . . . . . . . . . .    80
                12.4.3 Alias listings . . . . . . . . . . . . . . . . .    80
                12.4.4 Response message . . . . . . . . . . . . . . . .    80
                12.4.5 Limiting Requests  . . . . . . . . . . . . . . .    81
                    Maximum match . . . . . . . . . . . . . . . . . . .    81
                    Maximum time  . . . . . . . . . . . . . . . . . . .    81
                    Maximum size  . . . . . . . . . . . . . . . . . . .    81
                    Minimum speed (BPS) . . . . . . . . . . . . . . . .    81
                12.4.6 Limited hours  . . . . . . . . . . . . . . . . .    81
                    Limited . . . . . . . . . . . . . . . . . . . . . .    81
                    Start . . . . . . . . . . . . . . . . . . . . . . .    82




                    End . . . . . . . . . . . . . . . . . . . . . . . .    82
                Days  . . . . . . . . . . . . . . . . . . . . . . . . .    82
                12.4.7 Event restrictions . . . . . . . . . . . . . . .    82
                12.4.8 Protecting files and directories . . . . . . . .    82
                12.4.9 Request processor  . . . . . . . . . . . . . . .    83

        13 Swapping . . . . . . . . . . . . . . . . . . . . . . . . . .    83
            13.1 Complete path specifications . . . . . . . . . . . . .    84
            13.2 Loading programs in a DOS shell  . . . . . . . . . . .    84

        14 CRT environments . . . . . . . . . . . . . . . . . . . . . .    84

        15 Message Status Bits  . . . . . . . . . . . . . . . . . . . .    84
            Private . . . . . . . . . . . . . . . . . . . . . . . . . .    85
            Crash . . . . . . . . . . . . . . . . . . . . . . . . . . .    85
            Hold  . . . . . . . . . . . . . . . . . . . . . . . . . . .    85
            File  . . . . . . . . . . . . . . . . . . . . . . . . . . .    85
            File request  . . . . . . . . . . . . . . . . . . . . . . .    85
            Update request  . . . . . . . . . . . . . . . . . . . . . .    85
            Kill/sent . . . . . . . . . . . . . . . . . . . . . . . . .    85
            Trunc/sent  . . . . . . . . . . . . . . . . . . . . . . . .    85
            Delete/sent . . . . . . . . . . . . . . . . . . . . . . . .    86
            Direct  . . . . . . . . . . . . . . . . . . . . . . . . . .    86
            Immediate mail  . . . . . . . . . . . . . . . . . . . . . .    86
            Lock  . . . . . . . . . . . . . . . . . . . . . . . . . . .    86
            Sent  . . . . . . . . . . . . . . . . . . . . . . . . . . .    86
            No status . . . . . . . . . . . . . . . . . . . . . . . . .    86

        16 Mail routing . . . . . . . . . . . . . . . . . . . . . . . .    86
            16.1 Default routing  . . . . . . . . . . . . . . . . . . .    87
            16.2 Message status . . . . . . . . . . . . . . . . . . . .    87
            16.3 Host/Hub/Boss routing  . . . . . . . . . . . . . . . .    88
            16.4 Qualifying systems . . . . . . . . . . . . . . . . . .    88
            16.5 Route commands . . . . . . . . . . . . . . . . . . . .    89
            16.6 LIST specifications  . . . . . . . . . . . . . . . . .    91
            16.7 Using nodelist flags . . . . . . . . . . . . . . . . .    92
            16.8 File routing/forwarding  . . . . . . . . . . . . . . .    92
            16.9 Message forwarding . . . . . . . . . . . . . . . . . .    92
            16.10 Multiple zones  . . . . . . . . . . . . . . . . . . .    92
            16.11 Examples  . . . . . . . . . . . . . . . . . . . . . .    93
            16.12 Dynamic packing . . . . . . . . . . . . . . . . . . .    94
            16.13 Regarding points  . . . . . . . . . . . . . . . . . .    94
            16.14 Order of evaluation . . . . . . . . . . . . . . . . .    94
            16.15 TARGET vs. qualification  . . . . . . . . . . . . . .    95
            16.16 Restrictions  . . . . . . . . . . . . . . . . . . . .    95
            16.17 Macros  . . . . . . . . . . . . . . . . . . . . . . .    95
                MYZONE  . . . . . . . . . . . . . . . . . . . . . . . .    95
                MYNET . . . . . . . . . . . . . . . . . . . . . . . . .    95
                MYPOINTS  . . . . . . . . . . . . . . . . . . . . . . .    95
            16.18 Supported nodelist flags  . . . . . . . . . . . . . .    95

        17 EMSI and IEMSI . . . . . . . . . . . . . . . . . . . . . . .    96
            17.1 Passwords  . . . . . . . . . . . . . . . . . . . . . .    96
            17.2 Mail . . . . . . . . . . . . . . . . . . . . . . . . .    96
            17.3 IEMSI  . . . . . . . . . . . . . . . . . . . . . . . .    96

        18 Script language  . . . . . . . . . . . . . . . . . . . . . .    97
            18.1 What can I do with it? . . . . . . . . . . . . . . . .    97
            18.2 Commands . . . . . . . . . . . . . . . . . . . . . . .    97




            18.3 Labels . . . . . . . . . . . . . . . . . . . . . . . .   102
            18.4 Node block . . . . . . . . . . . . . . . . . . . . . .   102
            18.5 PC Pursuit . . . . . . . . . . . . . . . . . . . . . .   102
            18.6 How do I update PCP.DAT? . . . . . . . . . . . . . . .   103
            18.7 MNEMONICS  . . . . . . . . . . . . . . . . . . . . . .   103

        19 FDSERVER . . . . . . . . . . . . . . . . . . . . . . . . . .   103
            19.1 What is a FDSERVER request?  . . . . . . . . . . . . .   104
            19.2 Request message  . . . . . . . . . . . . . . . . . . .   104
                19.2.1 Internal commands  . . . . . . . . . . . . . . .   104
            19.3 Using it . . . . . . . . . . . . . . . . . . . . . . .   105
            19.4 Keeping calls to a minimum . . . . . . . . . . . . . .   105
            19.5 Security . . . . . . . . . . . . . . . . . . . . . . .   106

        20 Service requests . . . . . . . . . . . . . . . . . . . . . .   106
            20.1 Service requests vs FDSERVER . . . . . . . . . . . . .   106
            20.2 Setting up . . . . . . . . . . . . . . . . . . . . . .   106
            20.3 ^ - + ?  . . . . . . . . . . . . . . . . . . . . . . .   107
            20.4 Security . . . . . . . . . . . . . . . . . . . . . . .   107
            20.5 A word of wisdom . . . . . . . . . . . . . . . . . . .   107

        21 Global command-line switches . . . . . . . . . . . . . . . .   108
            21.1 A word of wisdom . . . . . . . . . . . . . . . . . . .   112

        22 Environment variables  . . . . . . . . . . . . . . . . . . .   113
            22.1 FDOPT  . . . . . . . . . . . . . . . . . . . . . . . .   113
            22.2 FDSWAP . . . . . . . . . . . . . . . . . . . . . . . .   113
            22.3 POINTNET . . . . . . . . . . . . . . . . . . . . . . .   113
            22.4 FMOVR and FDOVR  . . . . . . . . . . . . . . . . . . .   113
            22.5 TZUTC  . . . . . . . . . . . . . . . . . . . . . . . .   113

        23 Semaphore files  . . . . . . . . . . . . . . . . . . . . . .   114

        24 Batch files  . . . . . . . . . . . . . . . . . . . . . . . .   117
            24.1 Errorlevels  . . . . . . . . . . . . . . . . . . . . .   117
            24.2 Categories . . . . . . . . . . . . . . . . . . . . . .   117
            24.3 Loading BBS software . . . . . . . . . . . . . . . . .   118
            24.4 Different labels . . . . . . . . . . . . . . . . . . .   118
            24.5 Same label . . . . . . . . . . . . . . . . . . . . . .   119
            24.6 DOBBS.BAT  . . . . . . . . . . . . . . . . . . . . . .   120
            24.7 EXEBBS.BAT . . . . . . . . . . . . . . . . . . . . . .   120
            24.8 Flow (batch files) . . . . . . . . . . . . . . . . . .   121

        25 Multi-tasking  . . . . . . . . . . . . . . . . . . . . . . .   122
            25.1 NS16550  . . . . . . . . . . . . . . . . . . . . . . .   122
            25.2 DESQview . . . . . . . . . . . . . . . . . . . . . . .   122
            25.3 DoubleDOS  . . . . . . . . . . . . . . . . . . . . . .   123
            25.4 Multilink  . . . . . . . . . . . . . . . . . . . . . .   124

        26 Converting from other mail systems . . . . . . . . . . . . .   124

        27 Help systems . . . . . . . . . . . . . . . . . . . . . . . .   124

        28 Sample (PCP) script  . . . . . . . . . . . . . . . . . . . .   125

        29 Commercial inquiries . . . . . . . . . . . . . . . . . . . .   127

        30 Developer notes  . . . . . . . . . . . . . . . . . . . . . .   128




        31 Technical specifications . . . . . . . . . . . . . . . . . .   128

        32 Credits  . . . . . . . . . . . . . . . . . . . . . . . . . .   128




        1 SHAREWARE VERSION LICENCE AGREEMENT - "FFHA184k"

            1.  This is a licence agreement between you, the end user, and
                Joaquim Homrighausen. The FrontDoor 2.11 Shareware software
                and information attached hereto, hereafter "FD", is the
                property of Joaquim Homrighausen. Read the terms and
                conditions of this licence agreement carefully before using
                the software. If you for any reason, whatsoever, cannot
                accept the conditions in this agreement, you are not
                permitted to use FD.

            2.  You acknowledge and agree that FD is a proprietary product of
                Joaquim Homrighausen, protected by applicable copyright laws
                and international treaty provisions. You further acknowledge
                and agree that all rights, title, and interest in and to FD
                are and shall remain with Joaquim Homrighausen.

            3.  FD may be used for a period of thirty (30) days on a trial
                basis to allow you to determine its suitability for your
                particular application. After this period you MUST register
                each copy of FD that you run simultaneously. Site and Group
                registrations are available, and are dealt with on a case by
                case basis.

            4.  Registration entitles you to use FD and any future versions
                of FD for as long as you wish, subject to any special
                licensing conditions and/or applicable upgrade fees attached
                to future versions.

            5.  In the event that you are in violation of this licence
                agreement, you agree and accept that Joaquim Homrighausen may
                cancel your registration and any rights to use FD that you
                may have. In the case of a dispute over the licence
                agreement, you further agree and accept to fully reimburse
                Joaquim Homrighausen for legal and other expenses resulting
                from the dispute.

            6.  FD is provided "as is", without warranty of any kind or
                fitness for a particular purpose, either expressed or
                implied, all of are hereby explicitly disclaimed. Joaquim
                Homrighausen only guarantees that FrontDoor will occupy disk
                space.

                Joaquim Homrighausen's liability resulting from your use or
                inability to use FD is limited to the amount that the
                affected party has paid for it, or in the event that FD was
                registered with a third party for payment to Joaquim
                Homrighausen, liability is limited to the amount that was
                received by Joaquim Homrighausen from that third party.

            7.  Neither Joaquim Homrighausen nor any of his employees,
                agents, or other representatives are in any way obligated to
                provide future versions of, or support for, FD.





                                          1




            8.  You may freely distribute and copy FD provided that no fee is
                charged and the FD distribution archive contains unmodified
                copies of the original files as produced by Joaquim
                Homrighausen. Pay Bulletin Board Systems may, however, charge
                their normal fee provided that no additional charge for FD is
                levied. No part of FD may be modified, altered, reverse
                engineered, sold, or distributed in any form whatsoever which
                would involve some sort of trade without prior written
                permission from Joaquim Homrighausen.

            9.  FD may not be used in any unlawful or illegal manner.

            10. FD may only be used and registered by physical persons for
                use on equipment, including but not limited to telephone
                lines, electricity, hardware, and software, maintained and
                operated 100% by means of taxed personal income. FD may not
                be used to provide commercial services.
































                 All Joaquim Homrighausen products are trademarks or
              registered trademarks of Joaquim Homrighausen. Other brand
           and product names are trademarks or registered trademarks of    
                              their respective holders.

            Copyright 1986-1993 Joaquim Homrighausen; All rights reserved.

                                  September 25, 1993

                                          2




        2 Preface

        <C> as used in FrontDoor indicates that the feature is only available
        in the commercial version; <+> indicates that the feature is only
        available in the registered shareware version.

        Welcome to FrontDoor, the complete e-mail package. It is probably
        safe to say that an e-mail package, such as FrontDoor, is one of the
        most complex types of applications around. This manual is very
        straight forward and may seem hard to understand at first glance. If
        you get lost, or cannot understand something, go back and read the
        section you are having problems with, carefully.

        FrontDoor has been tested on more than four thousand systems for over
        six years. It will run under MS or PC DOS versions 3.1 and above;
        including OS/2 1.3, 2.0, and 2.1 DOS Mode. It runs under most LAN
        software; including Novell and LANtastic. It also runs under
        PC-MOS/386, VM/386, Windows, Windows NT, and in other multi-tasking
        environments such as DESQview.

        For technical specifications, see "Technical specifications".
        Although FrontDoor will run on most machines, there are a few
        restrictions and requirements.


            2.1 Hardware requirements

                o   An IBM PC, AT, i386, i486, PS/2 or 100% BIOS compatible.
                o   A hard disk with at least 1 MB available diskspace.
                o   An asynchronous modem capable of sending alphanumeric
                    messages such as CONNECT 2400.
                o   A DTE interface (computer <> modem) that supports CTS/RTS
                    handshaking (most cables/internal modems do).
                o   A monochrome or color monitor.
                o   384 KB of system memory.


            2.2 Software requirements

                o   MS or PC DOS 3.10 or above.
                o   A FOSSIL driver such as X00 or BNU.


            2.3 Additional equipment

            FrontDoor can take advantage of, but does not require, the
            following:

                o   EMS memory for overlays and EMS/XMS memory for program
                    image swapping.
                o   EGA/VGA extended screen modes such as 80x43/50 and
                    132x28.
                o   AT-style (extended) keyboard.





                                          3




            2.4 BBS software

            FrontDoor can be used as a front-end to many popular bulletin
            boards including TUBBS, PC Board, RemoteAccess, Maximus-CBCS,
            TCL, TPBoard, QuickBBS, SuperBBS, Phoenix RCS, Fido, Opus-CBCS,
            and WildCat!.


        3 Installation

        Several files are included in the distribution archive. This manual
        will walk you through the installation and configuration of the
        system. All path names and directories suggested here are not
        required. You can change them as you wish, but it is suggested that
        you use the examples shown for a start and then move on to change
        things as you become more familiar with the software. In the example,
        it is assumed that you are about to install FrontDoor on your C
        drive.


            3.1 CONFIG.SYS

            FrontDoor needs to have a few extra file handles allocated to
            keep some files open. Your CONFIG.SYS file should contain
            FILES=25 (or higher). If you do not know what handles means, that
            is okay, as long as you have the FILES=25 statement in your
            CONFIG.SYS file. If you are using multi-tasking software, your
            FILES= setting must usually be set to something higher than 25.

            You should also have BUFFERS=30 (or higher) in your CONFIG.SYS
            file to improve DOS' buffer performance. If you are using a disk
            cache, you should have BUFFERS=3 or something close to that.


            3.2 AUTOEXEC.BAT

            Add SET FD=C:\FD to your AUTOEXEC.BAT file. This will make sure
            FrontDoor can find all its system files. You may NOT have spaces
            between FD and =.


            3.3 Directories

            From your root directory (C:\) create a directory called FD. This
            is the main (ROOT) directory for FrontDoor. Change the active
            directory to FD. Create the following directories:

                NODELIST
                MAIL
                PACKETS
                FILES


            3.4 Files

            Copy FD.EXE, FD.OVR, FM.EXE, FM.OVR, FDNC.EXE and FDSETUP.EXE to
            C:\FD. The program files are now installed.

                                          4




            3.5 FidoNet

            If you are joining (or already an active in) FidoNet, you should
            obtain a copy of a recent FidoNet nodelist. The FidoNet nodelist
            can be found on many FidoNet systems under the name NODELIST
            followed by an extension.

            Place the uncompressed nodelist ASCII file in the C:\FD\NODELIST
            directory. The uncompressed nodelist is usually called
            NODELIST.nnn where nnn is three digits.


        4 Setup

        The Setup program, FDSETUP hereafter, is used to configure FrontDoor.
        Most functions and behavior of the Editor (FM), Mailer (FD), and
        Terminal are controlled from FDSETUP. When you start FDSETUP, it
        searches for the system file, SETUP.FD, in the directory pointed to
        by the FD environment variable.

        If the FD variable has not been set, FDSETUP searches the current
        directory for SETUP.FD. If it cannot open SETUP.FD, it will ask you
        if you want to create a new file or abort.


            4.1 FD environment variable

            The FD environment variable specifies where FDSETUP should search
            for SETUP.FD. If the FD environment variable is not set, FDSETUP
            will search the current directory for SETUP.FD. It is recommended
            that you add SET FD=<path> to your AUTOEXEC.BAT or other startup
            file. This allows FDSETUP, and the other FrontDoor programs, to
            locate SETUP.FD without having to be in the same directory.

                E.g. SET FD=C:\FD


            4.2 FD.SYS <> SETUP.FD

            The system file used by some earlier (1.99c and 2.00) versions of
            FrontDoor is called FD.SYS. Some FrontDoor specific utilities
            (TosScan 1.00 for example) and other programs may therefore
            require that you maintain a copy of FD.SYS. If you are using such
            software, make sure you copy SETUP.FD to FD.SYS in the FrontDoor
            root directory.


            4.3 Getting started

            To create a new SETUP.FD file, make the FrontDoor root directory
            the active directory by using the DOS command CD; type FDSETUP
            and press Enter. If you have set the FD variable, you do not have
            to change the active directory before invoking FDSETUP.

            FDSETUP will display a message saying something like "SETUP.FD,
            path or file not found". Press <Space> to create a new file.


                                          5




            4.4 Menus

            There are eight top-level (pull-down) menus. Each function and
            menu of FDSETUP will now be described.


                4.4.1 File

                Write SETUP.FD

                Forces FDSETUP to write the configuration file, SETUP.FD, to
                disk. This allows you to commit any changes you have made to
                your configuration without leaving FDSETUP.

                Shell to DOS

                Invokes a temporary DOS shell. Type EXIT and press <Enter> to
                return to FDSETUP. You can invoke a temporary DOS shell in
                FDSETUP by pressing <Alt-Z> in the middle of input fields,
                pull-down menus, selection fields, etc.

                Exit

                Returns you to DOS or the Mailer, depending on how FDSETUP
                was invoked. If you made any changes to your configuration,
                you will be asked if you want to make your changes permanent
                or abandon them. You can also exit FDSETUP by pressing <Esc>
                at any of the top-level menus.

                Enter your code

                Allows you to enter the registration code required to
                activate some registered-only features. Once you have
                succesfully entered your registration code, FDSETUP will not
                allow you to enter it again.


                4.4.2 Global

                Address

                    Address

                    Defines your network address and alternate network
                    addresses, or "also-known-as" (AKA). You must define at
                    least one network address (the first slot).

                    Site info

                    Defines your system's name, geographical location,
                    telephone number, maximum speed, nodelist flags, and the
                    name of your BBS software (if any).

                    The telephone number should be specified in international
                    format, eg. +352 316702 or "-Unpublished-" if you do not
                    wish to reveal this information to other systems.


                                          6




                    Domains

                    Specifies the name of a network zone. This should be
                    "fidonet" for all FidoNet Zones (currently 1 through 6).

                    At the moment, this is only used for the generation of
                    the ^AMSGID: kludge line and for inserting "^aVia"
                    information in messages forwarded by the Mailer (FD).

                    AKA..

                    Allows you to specify which AKA to use when corresponding
                    with certain zones and nets within zones.

                    I.e. if you are writing a message to someone in zone 2
                    and you have specified that you wish to use your 2:270/17
                    AKA for this, the Editor will automatically use 2:270/17
                    regardless of your current AKA setting.

                    This allows you to easily participate in multiple
                    networks.

                Filenames

                    System

                    Where the FrontDoor system files are stored. This should
                    NOT be a RAM disk. If you have followed the installation
                    instructions above, this should be C:\FD.

                    NetMail

                    Where NetMail messages are stored, i.e. the NetMail
                    folder. The Mailer unpacks received messages to this
                    directory. This should NOT be a RAM disk. If you have
                    followed the installation instructions above, this should
                    be C:\FD\MAIL.

                    Files

                    Where inbound (received) files are stored. This should
                    NOT be a RAM disk. If you have followed the installation
                    instructions above, this should be C:\FD\FILES.

                    SecFiles

                    Identical to Files above except that it is only used to
                    store files received during a secure (password protected)
                    mail session. If SecFiles isn't specified, the Mailer
                    will use the path specified for Files.

                    Packets

                    Where the Mailer stores its temporary mail packets. They
                    are created every time the Mailer runs a mail event and
                    are removed when the event ends.


                                          7




                    By putting the Packet directory on a RAM disk, you can
                    greatly improve the speed of packing and scanning
                    outbound mail.

                    It is recommended that you use a sub-directory on your
                    RAM disk since the number of directory entries in the
                    root directory of a drive is usually limited to a fairly
                    low number.

                    If you have followed the installation instructions above,
                    this should be C:\FD\PACKETS.

                    Log file

                    The log file. This is a complete filename, e.g.
                    C:\FD\FD.LOG. This is used by the Mailer (and can be used
                    by the Terminal in the registered version) to log its
                    activies such as received and sent files, call progress,
                    etc. You should NOT use a RAM disk for the log file as it
                    will disappear if the system reboots.

                    Banner

                    The contents of this file is displayed to human
                    (interactive) callers before the Mailer passes control to
                    your batch file to invoke the BBS software. This file is
                    not used if you are running in mail-only mode. You should
                    NOT use a RAM disk for the banner file.

                    Nodelist

                    Where the nodelist database is stored. The Nodelist
                    Compiler (FDNC) expects to find its control file(s) here.
                    The Mailer and Editor expects to find the compiled
                    nodelist database here. If this directory is not
                    specified, FrontDoor will use the SYSTEM directory
                    instead. The nodelist directory should NOT be located on
                    a RAM disk.

                    If you have followed the installation instructions above,
                    this should be C:\FD\NODELIST.

                    No BBS

                    This file is displayed to human callers if the Mailer
                    rejects their call. I.e. if you are running in mail-only
                    mode or if a mail event prevents interactive access to
                    your BBS.

                    MSG Base

                    Where the Editor expects to find the Hudson Message Base
                    files (MSGHDR.BBS, MSGTXT.BBS, MSGINFO.BBS, MSGIDX.BBS,
                    MSGTOIDX.BBS and LASTREAD.BBS). If you do not have any
                    folders with MsgBase status, you do not have to specify
                    this.


                                          8




                    Swapping

                    If you enable swapping to disk or there is not sufficient
                    XMS/EMS memory available. The Mailer and the Editor will
                    use this directory to store its swap file.

                    This setting can be overridden by the FDSWAP environment
                    variable (see "Environment variables").

        <C>         Semaphore

                    Where the Mailer and Editor creates and looks for the
                    various semaphore files (see "Semaphore files"). This
                    allows you to configure a multi-line and/or multi-user
                    system with different configurations to use the same
                    semaphore directory.

        <C>         MailExit

                    If specified, this file is created by the Mailer when it
                    has received mail and would normally have terminated with
                    an errorlevel indicating that mail has been received.

                    In a multi-line and/or multi-tasking environment, this
                    could be used to automatically invoke mail processing
                    software and run it in the background while the Mailer
                    continues its operation.

                General

                    Your country code

                    Your country code. Eg. USA=1, Sweden=46, Luxembourg=352.
                    This is used for telephone number translations. This is
                    related to the COUNTRY= command used in CONFIG.SYS. It
                    does not, however, have to be the same as your COUNTRY=
                    setting. FDSETUP's country code setting should always be
                    your real country code.

                    Screen flickers

                    FrontDoor attempts to detect if you have a CGA card that
                    causes flicker if software performs direct memory access
                    (DMA). The default for this setting is NO and you should
                    leave it alone unless you are seeing flicker on your
                    screen when you use the Mailer, Editor, and/or the
                    Terminal.

                    Use "fastkey"

                    Forces the Mailer, Editor, and the Terminal to speed up
                    the typematic rate of your keyboard. This is only valid
                    for machines with an AT- or compatible BIOS installed.

                    If you are using other keyboard speed-up utilities, leave
                    this to NO; otherwise, FrontDoor will restore the
                    typematic rate to the default (slow) when they terminate.

                                          9




                    Screen blanking

                    Prevents screen images from "burning in". If you are
                    using a monochrome monitor, data that is displayed often
                    in the same location on your screen can "burn in" and
                    leave ugly marks. Color monitors usually do not have this
                    problem.

                    Since the Mailer is active more than 80% of the day on
                    most systems, it may be wise to enable this option to
                    avoid "burn ins" of the Mailer's main display.

                    Blackout timer

                    Specifies how many seconds of inactivity should pass
                    before the screen is blanked. This option is only used if
                    screen blanking (previous page) has been enabled. You can
                    "light up" a blanked screen by pressing a key. The screen
                    will also be lit when the Mailer places outgoing calls
                    and when incoming calls are answered.

                    Extended keyboard

                    Specifies which type of keyboard you have (101/102 or
                    83/84). FDSETUP will attempt to "guess" which type of
                    keyboard you have, but some BIOS flavors does not
                    properly indicate the type. This allows you to override
                    what FDSETUP detects.

                    Force 24-hour fmt

                    Allows you to force the Mailer and the Editor to display
                    the time in 24-hour format even if you are located in a
                    country that uses the 12-hour format, such as the USA.

                    Monochrome mode

                    Forces FDSETUP to assume monochrome color mode (as if you
                    would have specified FDSETUP -m on the DOS command-line).

                Users

                Allows you to specify user names and access levels. The
                default name of the first user is System Operator. You should
                change this to your own name.

        <+>     There are three different access levels. Supervisor,
                Administrator and User.

                A user with Supervisor access can override any restrictions
                on folders and messages. He/she can also change all settings
                regardless of passwords. You should only have one user with
                Supervisor access, but FDSETUP will allow you to define more
                than one. At least one user with Supervisor access MUST exist
                and is required to add any additional users.



                                          10




                A user with Administrator access cannot override any
                restrictions on folders and messages. He/she has to enter
                passwords for protected items before they can be changed.

                A user with User access cannot override any restrictions on
                folders and messages. The only setting he/she can change in
                FDSETUP is his/her own password.

                >>> The unregistered shareware version only allows you to
                    define one user and forces the access level to that of
                    Supervisor.


                4.4.3 Mailer

                Miscellaneous

        <+>         Mail from unlisted systems

                    Defines whether or not the Mailer should accept incoming
                    calls from systems not listed in your nodelist database.
                    If this option is disabled (set to NO) and an unlisted
                    system calls in, the Mailer will terminate the call
                    immediately.

        <C>         Mail from "unprotected" systems

                    Defines whether or not the Mailer should accept incoming
                    calls from systems for which you do not have a session
                    level password defined. If this option is disabled (set
                    to NO) and an unprotected system calls in, the Mailer
                    will terminate the call immediately.

        <+>         Mail from unlisted points

                    The Mailer will by default accept calls from points of
                    other systems whether or not they are present in your
                    nodelist database; provided the point system's boss
                    passes the required criteria.

                    You can, however specify that you do not want the Mailer
                    to accept calls from points that cannot be found in the
                    nodelist database. If this option is disabled (set to NO)
                    and a point for which you have no entry in your nodelist
                    database calls in, the Mailer will terminate the call
                    immediately.

                    Kill empty received messages

                    Specifies that you want the Mailer to kill empty messages
                    (messages with no text in its body) when they are
                    unpacked from received mail packets.






                                          11




                    Terminal only (no mail)

                    If enabled, the Mailer will invoke the Terminal as soon
                    as it is loaded. This setting can be overridden with the
                    -M command line switch.

                    Mail only (no BBS)

                    If enabled, the Mailer will not accept human callers
                    under any circumstances. Use this option if you do not
                    have a BBS or similar software running "below" the
                    Mailer.

                    Present all AKAs to remote system

                    If you have more than one AKA address, the Mailer will by
                    default attempt to pickup mail destined for all your
                    addresses during a mail session.

                    This can be disabled so that only one address is
                    presented to the remote system. Which address is actually
                    presented is determined by the AKA matching table
                    (described above).

                    Trigger exit upon receipt of netmail

                    The Mailer will by default only trigger (set) the exit
                    flag when compressed (following the ARCmail 0.60
                    standard) mail is received. If this option is enabled,
                    the exit flag will be triggered (set) when NetMail
                    packets (files ending with the extension .PKT) have been
                    received. Whether or not the Mailer will actually exit is
                    controlled by event behaviors (see "Events") and the mail
                    exit errorlevels.

                    Trigger exit upon receipt of ANY file

                    Similar to the above option, but will trigger exit as
                    long as any (file) data has been received.

                    Print received messages

        <C>         If enabled, the Mailer will print messages unpacked from
                    received mail packets.

                    Busy retries

                    Defines the maximum number of times the Mailer will
                    attempt to call a system during an event (see "Events")
                    if the system is busy or does not answer on the first
                    call. See the section about the Mailer for further
                    details regarding call progress.






                                          12




                    Resend retries

                    Defines the maximum number of times the Mailer will
                    attempt to transfer mail to a system during an event if
                    the first attempt fails. See the section about the Mailer
                    for further details regarding call progress.

                    Retry delay

                    Defines the minimum number of seconds the Mailer will
                    wait between outgoing calls. This is used in conjunction
                    with a random timer to avoid two Mailers calling each
                    other at the same time (and thus causing both telephone
                    lines to be engaged).

                    Delay before first call

                    The Mailer will by default attempt to place the first
                    outgoing call as soon as possible. If this option is
                    enabled, it will delay the first call.

                    Days to keep mail history

                    Number of days to retain entries in the inbound/outbound
                    history files. The Mailer removes all entries older than
                    this value from the history files every morning (at first
                    opportunity after midnight).

                    Seconds before passing to BBS

                    Defines the number of seconds the Mailer will wait before
                    assuming a human caller. Unless the Mailer receives two
                    consecutive escape (ASCII 27) characters, it will attempt
                    to establish a mail session for the amount specified
                    here. The minimum and default value is 11 seconds. The
                    maximum value is 60 seconds.

                    Minimum undialable cost

                    The minimum cost of a call for a system to be processed
                    by the undialable handler. The undialable handler is
                    discussed in a separate section.

        <C>         Honor Return Receipt Requests (RRQ)

                    Specifies whether or not the Mailer should generate a
                    Return Receipt for received messages with the RRQ flag
                    set. The RRQ flag is discussed in the Editor section.

                Log

                Defines the various level of logging. All messages will
                appear on the screen, the log options defines which of them
                ends up in the log file.




                                          13




                File requests

                Controls how the Mailer treats inbound File and Update
                Requests. A separate section explains File and Update
                Requests in detail.

        <+>     FDServer

                If no password is specified in FDSETUP, the FDSERVER function
                is inactive (disabled). The FDSERVER function is described in
                a separate section.

                External mail

                When the Mailer processes an incoming call, all received
                characters are processed for a possible match with any of the
                external mail "wake-up" sequences (strings), and if a match
                is made, the Mailer exits with the specified errorlevel of
                the matching string.

                This allows you to run alternate mail handlers behind the
                Mailer, such as UFGATE and Waffle to process INTERNET/UUCP
                mail. Note that the call is not terminated when using the
                external mail interface, the Mailer simply exits with the
                specified errorlevel. This option is NOT intended for
                EchoMail processors, etc.

                To enter characters with an ASCII code below 32 (Space), hold
                down the <Alt> key, enter the ASCII code on the numerical
                keypad and release the <Alt> key.

                Display

                    Mail waiting flashing

                    When there is new mail waiting, the text "Mail" will
                    flash on the Mailer screen. The flashing can be disabled
                    with this option.

                    Display clock

                    Specifies whether or not you want the current date and
                    time displayed in the top right corner of the Mailer
                    screen.

                    Display timestamp

                    Specifies whether or not you want the Mailer to display
                    the time to the left of each line displayed in the main
                    activity window. This setting does not affect what is
                    being written to the log file.

                    Screen size

                        25

                        25 line mode.

                                          14




                        43/50

                        43/50 line mode. Only available for systems with EGA
                        and VGA cards.

                        Auto

                        Specifies that the Mailer should attempt to
                        automatically adapt to whatever the current screen
                        size is when it is started.

                        This also means that the Mailer will not attempt to
                        reset the screen mode when it is terminated.

        <+>             Custom

                        Allows you to specify computer register values to
                        send to the INT 10h (Video BIOS) to set and reset the
                        screen.

                Colors

                Allows you to choose between the default monochrome (black
                and white) and the default color sets. You can also choose to
                customize the colors to your own taste.

                Hidden dial info

                Allows you to hide portions of telephone numbers that
                otherwise would be displayed when the Mailer places an
                outgoing call. E.g. The Mailer calls 352-316702, if you had
                one of the hidden dial info strings set to 352- the displayed
                number would be 316702.

                Function keys

                Allows you to define up to 20 (24) programs, etc. to invoke
                from the Mailer when any of the functions keys are pressed.
                The first 10 (12) function keys are accessed through <F1> -
                <F10> (F12), the second 10 (12) function keys are accessed
                through <Shift-F1> - <Shift-F10> (F12).

                    Title

                    The title to appear on the screen when you press <Alt-K>
                    from the Mailer's main screen. This is also written to
                    the log file when a function key is pressed.

                    Action

                    The program to invoke or errorlevel to exit with. To
                    specify more than one program, separate them by
                    semicolons (;). To exit with an errorlevel, specify
                    ?<errorlevel>.

                        E.g.    LIST C:\FD\FD.LOG;DEL C:\FD\FD.LOG


                                          15




                    would load the program LIST and pass C:\FD\FD.LOG as the
                    parameter. When the LIST program terminates, the Mailer
                    would proceed to the next command, which in this case
                    removes C:\FD\FD.LOG.

                        ?255

                    Would force the Mailer to terminate with an errorlevel of
                    255.

                    Pause

                    Specifies whether or not you want the Mailer to pause
                    when the invoked program(s) terminates.

                    Check

                    Specifies whether or not the Mailer should rescan the
                    NetMail folder when the invoked program(s) terminates.

                    Swap

                    Specifies whether or not the Mailer should swap itself
                    out of memory prior to invoking the specified commands.

                >>> To create a DOS shell that does not force a re-scan of
                    the NetMail folder, specify C:\COMMAND.COM (or wherever
                    you have your copy of COMMAND.COM stored) as ACTION and
                    set CHECK to NO.

                Errorlevels

                This section allows you to invoke BBS software, or other
                similar software, when an incoming call is established and
                the Mailer has determined that it is not a mail call. It also
                allows you to define an errorlevel to exit with when mail has
                been received.

                If a baudrate related errorlevel is zero, the Mailer will
                display a message to human callers saying that your system
                does not support non-mail calls at that speed and then
                terminate the call. If you are running in mail-only mode, the
                Mailer will never accept non-mail (human) calls.

                If the RECEIVED MAIL errorlevel is zero, the Mailer will
                never exit when mail has been received. Whether or not the
                Mailer will actually exit when it has received mail is
                determined by the current event behavior and whether or not
                the received file(s) indicated mail.

                The CREATE .BAT FILE option allows you to simplify BBS
                operation. If it is enabled, the Mailer will create a batch
                file containing the current baudrate, the COM port used, the
                number of minutes left to the next system event, etc. This is
                described in a separate section.



                                          16




                Audio control

                The Mailer can sound alarms and make other noises when
                certain events occur, such as received mail, incoming human
                callers, fatal errors, etc. This section allows you to
                control which sounds should be active and when audio should
                be active.

                Swapping

                Determines whether or not you want the Mailer to use swapping
                when executing external programs. You can disable the use of
                EMS/XMS memory for the swap function. The swap function is
                explained in the Miscellaneous section.

        <C>     Protection

                Allows you to protect certain functions of the Mailer, such
                as access to the DOS shell, Editor, Nodelist compiler,
                Terminal, etc. with a password.

        <C>     Fax

                Allows you to control how the Mailer should handle incoming
                fax calls.


                4.4.4 Editor

                Miscellaneous

        <C>         Delete original (Conference)
        <C>         Delete original (Local)
        <C>         Delete original (NetMail)

                    Determines if the Editor should ask "Delete original
                    message" when replying to messages in EchoMail
                    (Conference), Local, and NetMail-type folders.

                    Show hard CRs

                    If enabled, the Editor will show hard CRs in messages.
                    The display of hard CRs is disabled by default and can be
                    toggled from within the Editor.

                    Margin

                    Specifies the margin at which the Editor should
                    automatically wrap text when you enter and quote (reply)
                    messages. The default value, 60, should not be changed in
                    most cases.

                    When you read messages in the Editor, it will use all
                    available columns (80, 132, etc.) as the wrap margin.




                                          17




        <C>         Honor CFM

                    Specifies whether or not the Editor should generate a
                    Return Receipt for received messages with the CFM
                    (Confirmation Receipt Request) flag set. The CFM flag is
                    discussed later in the Editor section.

        <C>         New mail semaphores

                    Specifies whether or not the Editor should create the new
                    mail semaphores FMNEWNET, FMNEWCNF, and FMNEWLOC upon
                    exit when you have entered one or more messages.

                NetMail folder

        <+>         Restricted

                    Specifies if the NetMail folder should be restricted. If
                    you enable this, users with User or Administrator access
                    can only read private messages addressed to their
                    usernames.

        <+>         Read-only

                    Prevents users with User or Administrator access from
                    writing messages in the NetMail folder. The definition of
                    writing includes forwarding and moving of messages to the
                    NetMail folder.

        <+>         Export OK

                    Defines whether or not users with User or Administrator
                    access can export messages from the NetMail folder. The
                    definition of export includes moving, copying, and export
                    to disk.

                    Use tables

                    Defines whether or not the translation tables should be
                    active by default in the NetMail folder. This can be
                    toggled from within the Editor.

                    Crash

                    If the Crash status bit should be set by default on
                    locally created messages.

                    Direct

                    If the Direct status bit should be set by default on
                    locally created messages.

                    Hold

                    If the Hold status bit should be set by default on
                    locally created messages.


                                          18




                    Private

                    If the Private status bit should be set by default on
                    locally created messages.

                    Kill/Sent

                    If the Kill/sent status bit should be set by default on
                    locally created messages.

        <+>         Use Zonegates

                    Determines if the Editor should ask you whether or not
                    you want to send inter-zone messages via the zonegate,
                    never send messages via the zonegate, or always send
                    inter-zone messages via the zonegate.

                Keyboard macros

                Allows you to define up to 20 (24) strings. These can be used
                to insert common text, such as name signatures, etc. while
                editing messages. The first 10 (12) function keys are
                accessed through F1-F10 (F12), the second 10 (12) function
                keys are accessed through Shift F1-F10 (F12).

                The Editor macro language is discussed in the section about
                how to operate the Editor.

                Origin lines

                Appended to messages you create in Conference-type folders to
                show the origin of a message. These should include the name
                and location of your system if possible.

                You can choose default origin lines for all Conference-type
                folders. You can also choose a different origin line from
                within the Editor.

                Whether or not the origin line is appended to messages you
                enter in Conference-type folders is controlled by the Echo
                info status bit for each folder.

                Display

                    Screen size

                        25

                        25 line mode.

                        43/50

                        43/50 line mode. Only available for systems with EGA
                        and VGA cards.




                                          19




                        Auto

                        Specifies that the Editor should attempt to
                        automatically adapt to whatever the current screen
                        size is when it is are started. This also means that
                        the Editor will not attempt to reset the screen mode
                        when it is terminated.

        <+>             Custom

                        Allows you to specify computer register values to
                        send to the INT 10h (Video BIOS) to set and reset the
                        screen.

                Colors

                Allows you to choose between the default monochrome (black
                and white) and the default color sets. You can also choose to
                customize the colors to suit your own needs.

                Xlat.In and Xlat.Out

                Defines the translation tables to use wherever the
                translation table status bit is active. This is used to
                translate language specific 8-bit ASCII characters to 7-bit
                ASCII when writing messages to disk and vice versa when
                reading messages from disk.

                The In table is used when reading messages from disk and the
                Out table is used when writing messages to disk.

                FDSETUP automatically creates reasonable defaults for most
                countries when it creates a new SETUP.FD file. If you are
                located in an English speaking country, you do normally not
                have to worry about translation tables.

                Swapping

                Determines whether or not you want the Editor to use swapping
                for its DOS shell. You can disable the use of EMS/XMS memory
                for the swap function. The swap function is explained in a
                separate section.

        <C>     Fax

                Settings related to internal fax support.


                4.4.5 Terminal

                Miscellaneous

                    Init

                    An additional modem initialization string, sent to the
                    modem as soon as the Terminal is started.


                                          20




                    If you start the Terminal directly from DOS (FD -TERM) or
                    have set the Terminal-only option in FDSETUP, the
                    Mailer's initialization strings are first sent to the
                    modem.

                    Download

                    Default download path. Files that you receive (download)
                    during a Terminal session will by default end up here.

                    Upload

                    Default upload path.

                    Editor

                    Allows you to install an Editor or file listing program
                    and invoke it from the Terminal. The Terminal will prompt
                    your for optional parameters, such as filenames, etc.
                    This can also be used to invoke external protocols or
                    external protocol menu programs.

                    Protocol

                    Zmodem, SEAlink, Telink, or Xmodem. Defines the default
                    transfer protocol to use for file transfers in the
                    Terminal.

                    Emulation

                    ANSI, TTY, VT100 or VT52. Defines the default Terminal
                    emulation protocol to use in the Terminal. Note that the
                    Terminal's ANSI protocol supports the AVATAR/0+ (AVT/0+)
                    emulation protocol.

                    AVATAR/0+

                    Allows you to disable the support for AVATAR/0+ sequences
                    in ANSI emulation. This can be toggled from within the
                    Terminal.

                    Buffer

                    The size, in KB, of the scroll-back buffer. The scroll-
                    back buffer stores information that has "rolled off" the
                    top of the screen during Terminal sessions.

                    Connect noise

                    Whether or not the Terminal should make noise when a
                    connection has been established.

                    Transfer noise

                    Whether or not the Terminal should make a noise after
                    file transfers.


                                          21




                    Use tables

                    Whether or not the Terminal translation tables should be
                    active by default. See Editor > Xlat.In for a detailed
                    explanation of translation tables.

                    Auto Zmodem

                    Whether or not the automatic Zmodem download (receive)
                    function should be enabled by default.

                    Local echo

                    Whether or not the Terminal should echo typed characters
                    to your screen by default.

                    Wrap around

                    Whether or not the Terminal should move the cursor to the
                    beginning of a new line when it reaches the end of the
                    previous line.

                    Delay

                    Number of seconds to wait between outgoing calls if the
                    number you dialed was busy or did not answer. If there is
                    more than one entry in the dial queue, the delay is
                    ignored and the Terminal proceeds to the next number in
                    the queue.

        <+>         Logging

                    Allows you to enable logging of file transfers, dialed
                    numbers, time spent on-line to systems, etc. Similar to
                    the Mailer's log output.

                Display

                    Screen size

                        25

                        25 line mode.

                        43/50

                        43/50 line mode. Only available for systems with EGA
                        and VGA cards.

                        Auto

                        Specifies that the Terminal should attempt to
                        automatically adapt to whatever the current screen
                        size is when it is are started. This also means that
                        the Terminal will not attempt to reset the screen
                        mode when it is terminated.


                                          22




        <+>             Custom

                        Allows you to specify computer register values to
                        send to the INT 10h (Video BIOS) to set and reset the
                        screen.

                Keyboard macros

                Allows you to define up to 20 (24) macro strings. These can
                be used to transmit common text, such as names and passwords,
                etc. The first 10 (12) function keys are accessed through
                <Shift-F1> - <Shift-F10> (F12), the second 10 (12) function
                keys are accessed through <Ctrl-F1> - <Shift-F10> (F12). This
                is referred to as the default macro set.

                To enter characters with an ASCII code below 32 (space), hold
                down the <Alt> key, enter the ASCII code on the numerical
                keypad and release the <Alt> key.

                Xlat.In and Xlat.Out

                See Editor > Xlat.In for a detailed explanation of
                translation tables. The Xlat.In table is used for characters
                received from the modem (remote). The Xlat.Out table is used
                for characters typed on the keyboard.

                IEMSI Profile

                Defines the default IEMSI (Interactive Electronic Mail
                Standard Information) profile used to negotiate interactive
                EMSI sessions with BBS software supporting it.

                    Active

                    Determines whether or not IEMSI support should be active
                    by default.

                    Name

                    The username you wish to use. If this field is empty, the
                    ACTIVE field (above) is automatically toggled to "NO".

                    Handle

                    The handle you wish to use, or empty if none.

                    Password

                    The password you wish to use.









                                          23




                    Hot-keys
                    Quiet
                    Pausing
                    Editor
                    News
                    New mail
                    New files
                    Screen Clr

                    Specifies default user profile options, allowing you to
                    customize the BBS or on-line service's behavior.

                    The Terminal allows you to configure separate profiles
                    for each individual telephone number in the Terminal
                    Phone Directory.


                4.4.6 Modem

                This option is used to configure your modem for use with
                FrontDoor. Modems are discussed in a separate section.


                4.4.7 Printer

        <C>     The printer configuration can only be changed in the
                commercial version. The shareware version defaults to using
                LPT1.


                4.4.8 Manager

                The managers are used to define events, session level
                security, file protection (for file requests), your message
                folders, and strings to be sent to the modem when calling
                specific systems.

                All managers require that the SYSTEM path has been defined
                since they store their data files (EVENT.FD, PASSWORD.FD,
                REQUEST.FD and FOLDER.FD) in that directory.

                Event Manager

                Events are discussed in a separate section.


                Folder Manager

                Folders are used to define different areas (directories, or
                boards for the Hudson Message Base) so that you can use the
                Editor to read and write messages in those areas. The Editor
                only knows about one folder by default. It is defined in the
                Filenames section of FDSETUP (described above) and is
                referred to as the NetMail folder.




                                          24




                The folder manager has two modes. The first is the view mode,
                which is self explanatory. The second mode is the edit/create
                mode and is accessed by pressing the Ins key. It will now be
                described.

                    Status

                    The status and type of the folder.

                    Origin

                    The default origin line to use. This is only used for
                    Conference-type folders with the Echo info status
                    enabled. Origin lines are used to identify the origin of
                    a message in Conference conferences. This is required
                    because conference mail is not a point to point
                    environment, like a telephone conversation or NetMail
                    exchange.

                    Mail conferences are usually widespread and can have an
                    unlimited number of participating systems.

                    Title

                    The title appearing in the folder list when you select a
                    new active folder in the Editor.

                    Board/Path

                    Depending on the type of the folder, this is either the
                    Hudson Message Base board number or the DOS path
                    (directory) where the messages for this folder should be
                    stored.

        <+>         Users

                    Defines which users should have access to this folder. If
                    a user does not have access to a folder, it will not show
                    up on his/her list of available folders.

                    Password

                    Defines whether or not access to the folder is protected
                    by a password. You can allow users to access a folder,
                    and the password protect it.

                    Use AKA

                    Defines which address (AKA) the Editor should use for the
                    folder. This is only important for Conference-type
                    folders with the Echo info status enabled. The address is
                    a part of the origin line.






                                          25




                    Folder status

                        Restricted

                        If enabled, users can only read Private messages
                        addressed to their username. Public messages are not
                        affected by this.

                        Echo info

                        Whether or not an origin line should be appended to
                        newly created messages. See Origin (above) for more
                        information.

                        Export OK

                        See NetMail folder > Export OK described above.

                        MsgBase

                        Specifies that the folder is of the Hudson Message
                        Base type, rather than a directory with .MSG message
                        files. The Hudson Message Base (HMB) is used by
                        several BBS packages, such as RemoteAccess.

                        Translate

                        Enables the translation tables for the folder. They
                        can be toggled on/off from within the Editor.

                        Private

                        Specifies that the Private status should be allowed
                        (and the default) for messages created in the folder.
                        This should NOT be used in Conference-type folders
                        unless the conference explicitly allows this.

                        Read-only

                        See Netmail folder > Read-only described above.

        <C>             No check

                        Determines if the Editor should access the specified
                        path when check for unread mail. This allows you to
                        create folders that holds messages on removable
                        media, e.g. floppy disks, that is not always
                        accessible to the Editor.

        <C>             Force CR

                        Forces the Editor to append a hard CR to all lines
                        instead of letting paragraphs flow. Some INTERNET
                        mail environments require that the line length does
                        not exceed a certain limit.



                                          26




                        Conference

                        Defines the folder as a Conference folder (as opposed
                        to a Local or NetMail-type folder).

        <C>             NetMail

                        Defines the folder as NetMail-type folder (as opposed
                        to an Conference or Local-type folder). This enabled
                        nodelist lookups, carbon copies, etc.

                        Local

                        Defines the folder as a Local folder (as opposed to
                        an Conference or NetMail-type folder). This is
                        usually used to access local BBS message areas.

                    Security

                    The security manager is used to define session level
                    passwords for other systems. It can also be used to
                    explicitly refuse File/Update Requests and Mail from a
                    system, and to disable/enable specific protocol and
                    handshake options to fine tune your outbound mail
                    sessions.

                    Session level passwords are used to protect the receiving
                    (called) system in a mail session, and calling system
                    during an outbound EMSI session, to ensure that the
                    calling system really is what it appears to be. Anyone
                    can setup a Mailer, like FrontDoor, and send you mail. If
                    there is mail waiting for the address they are using,
                    your system will by default attempt to send it.

                    You should setup session level passwords for all your
                    common mail links, such as conference mail distribution
                    systems, etc.

                        System

                        The system address of the remote system. Eg.
                        2:270/17.

                        Password

                        Defines the session level password that your system
                        will present when calling the specified system and
                        the password that your system requires to establish a
                        mail session with the specified system.

                        Note that some mailer software treat passwords case
                        sensitive, ie. ALLAN is not treated like AlLaN. The
                        FrontDoor Mailer will treat passwords case
                        insensitive on incoming (inbound) calls. They will,
                        however, be sent EXACTLY as you have defined them
                        here.


                                          27




                        You do not have to specify a password to use any of
                        the other options.

                        FREQs

                        Whether or not the specified system is allowed to
                        make File/Update Requests (see "File Requests").

                        Mail

                        Whether or not your system will allow the specified
                        system to call your system.

                        >>> Note that by disabling (setting it to "NO") this
                            option, you may be in violation of network
                            policy.

                        EMSI

                        Whether or not you want the Mailer to attempt to
                        negotiate an EMSI session when it calls the specified
                        system.

                        FTS-1

                        Whether or not you want the Mailer to attempt to
                        negotiate an FTS-1 session when it calls the
                        specified system.

                        Zap

                        Whether or not you want the Mailer to use the
                        ZedZap/Zmodem protocol when negotiating an FTS-6
                        (YooHoo) session. If this is set to "NO", the
                        DietIFNA protocol (Telink/SEAlink) will be used
                        during YooHoo sessions with the specified system.

                        YooHoo

                        Whether or not you want the Mailer to attempt to
                        negotiate an FTS-6 session when it calls the
                        specified system.


                        Notes regarding protocols

                        The Mailer will by default attempt to negotiate a
                        mail session in the following order:

                            1.  EMSI
                            2.  FTS-6 (YooHoo), ZedZap/Zmodem
                            3.  FTS-6 (YooHoo), DietIFNA
                            4.  FTS-1

                        The Mailer will ignore any entries in the security
                        manager with inactive status.


                                          28




                    Request Manager

                    The request manager is used to protect file requests.
                    File and Update Requests are discussed in a separate
                    section.


        5 The nodelist and the nodelist compiler

        The nodelist is FrontDoor's telephone directory and is used for
        several purposes. Among these are to allow you to perform name
        lookups of other SysOps, to retrieve information about remote
        systems, such as the maximum supported baudrate, modem flags, and
        system capability flags, to check if a remote system is known to your
        system or should be treated as an unlisted system.

        The Mailer requires that a nodelist be present whereas the Editor and
        the Terminal can both be used without one, if so required. The
        typical FidoNet nodelist contains over 20.000 systems and has a
        fairly straight forward structure as follows.

            Zone

            Usually a large geographical area, such as North America, Europe,
            Australia and New Zealand, etc. At the time of the release of
            this package, the following FidoNet Zone numbers have been
            allocated:

                1   North America (including Canada)
                2   Europe
                3   Australia, Tasmania, and New Zealand
                4   Latin America
                5   Africa
                6   Asia

            Region

            Usually a somewhat smaller geographical area, such as a country
            or part of a (large) country. A collection of regions make up one
            zone.

            Net

            Usually a collection of systems local to each other. Typically a
            city and in some cases including its suburbs. A collection of
            nets make up one region.

            Node

            A single system within a net.








                                          29




            Point

            A single system belonging to a node. Typically, a point is
            similar to a user logging on to a BBS system using his/her
            terminal program, with the main difference being that a point
            performs most of his/her activities offline and use smart
            software to collect and transit his/her mail.


            5.1 Hosts and hubs

            The coordinator of a net is called the host or NC for Network
            Coordinator. The host is responsible for maintaining the nodelist
            segment for his/her net and to act as an inbound NetMail gateway
            for the systems in his/her net ("host routed mail").

            In a large net, it is quite common that "sub-hosts", called hubs,
            are set-up to aid in mail distribution within the net. In other
            words, a hub has the same function for systems in a network that
            a host has for (remote) systems outside the same network.


            5.2 Compiling a nodelist

            Before FrontDoor can use the information in a nodelist, it must
            be compiled with the FrontDoor Nodelist Compiler (FDNC). FDNC
            will process the specified nodelist file(s) and generate database
            information and index files.

            The nodelist that FDNC needs to process is often referred to as
            the raw nodelist. It should not have been processed by Xlatlist,
            Parselst or a similar utility; but only be the nodelist you
            receive each week (if you are a FidoNet node) from your host.

            Grab a somewhat recent version of a nodelist and decompress it.
            Place the resulting file (such as NODELIST.228) in the NODELIST
            directory. Create a file called FDNODE.CTL with your a text
            Editor and place it in the same directory. You can also use the
            sample file included in the FrontDoor distribution package and
            modify it to suit your needs.


                5.2.1 FDNODE.CTL

                FDNODE.CTL is FDNC's control file. It is used to control how
                FDNC processes the nodelist files, for dial translation and
                cost calculation. The order of commands does not matter. All
                commands are case insensitive.

                    POINTLIST <FILENAME> [BOSS]

                    This option allows you to add points to your nodelist
                    database. The optional BOSS address is required if
                    FILENAME does not contain a BOSS entry and should not be
                    specified if FILENAME contains a BOSS entry.



                                          30




                    If you only have one file with point entries, you can
                    name it FDPOINT.PVT. FDNC will automatically use this
                    file if it is found in the NODELIST directory. If you use
                    one or more POINTLIST statements, FDNC will merge all
                    specified files into FDPOINT.PVT, overwriting its
                    contents. A separate chapter discusses the point concept.

                    PVTLIST <FILENAME> [ZONE]

                    Similar to the POINTLIST command, but FILENAME contains
                    one or more regular nodes. The optional ZONE number is
                    required if FILENAME does not contain a ZONE entry and
                    should not be specified if FILENAME contains a ZONE
                    entry. The optional ZONE number is only supported for the
                    first PVTLIST statement. FDNC accepts the POINT keyword
                    in private nodelists.










































                                          31




                    If you only have one file with additional node entries,
                    you can name it FDNET.PVT. FDNC will automatically use it
                    if it is found in the NODELIST directory. Note that if
                    you use one or more PVTLIST statements, FDNC will merge
                    all specified files into FDNET.PVT, overwriting its
                    contents.

                    Note that FILENAME for POINTLIST and PVTLIST may contain
                    wildcard characters (* and ?). FDNC will use the most
                    recent (by comparing the timestamp of the matching files)
                    file.

                    SWEPULSE

                    This command was added to handle the somewhat screwed up
                    method Swedish pulse exchanges handles dialing. Most
                    modem manufacturers uses the British standard for pulse
                    dialing, which is not compatible with Swedish pulse
                    dialing. If you use SWEPULSE in FDNODE.CTL, telephone
                    numbers will be properly translated. Do NOT use this
                    command unless you live in Sweden and have to use pulse
                    dialing.

                    PHONE <ADDRESS> <NUMBER>

                    Some systems are listed as PVT (private) in the nodelist,
                    in which case there is no telephone number available (the
                    text -Unpublished- is used in place). This, of course,
                    means that the Mailer cannot call a system listed as PVT.
                    If you have the phone number of a PVT listed system, or
                    wish to override the telephone number listed in the
                    nodelist, you can use the PHONE command.

                    ADDRESS is a fully qualified address (e.g. 2:270/17).
                    NUMBER is an untranslated (raw) telephone number (e.g.
                    352-355-936). If the PHONE command is used, FDNC will
                    remove possible DOWN, HOLD and PVT flags for the
                    specified system.

                    USE ZONE <ZONE>[<ZONE> <ZONE>..]

                    This command controls which zones FDNC should include in
                    the nodelist and username index files. The default is to
                    include all encountered zones. This does not affect the
                    contents of raw nodelist files, only what information
                    ends up in the nodelist and username index files.

                    DIAL <NATL PREFIX>/<SUFFIX> <INTL PREFIX>/<SUFFIX>

                    Indicates the start of the dial translation table. All
                    four parameters are optional and are only used if no
                    other translation applies for a telephone number.






                                          32




                    If you only want to use a national (NATL) prefix/suffix,
                    you must specify the / character for the international
                    (INTL) prefix/suffix to indicate no special treatment.
                    The same applies if you only want to use an INTL
                    prefix/suffix.

                        ;   prefix
                        ;   prefix/suffix
                        ;   /suffix
                        ;
                        DIAL    /   00          ; Add INTL prefix to all INTL
                                                ; numbers.
                            352-                ; Strip country code
                            61-     0061-/X2    ; Send X2 to modem for
                                                ; Australia
                            46-8    /391        ; Append (suffix) 391 to all
                                                ; numbers in Stockholm
                                                ; Sweden.
                        END

                    END is required to terminate the dial translation table.

                    If you need to strip the search value from a number, you
                    do not have to put anything after it. In other words, if
                    you need to strip 1-305-596 from all number, you enter
                    that string with no translation. Comments are ignored and
                    must be preceded by a semicolon.

                        DIAL    12345-1- 00
                            ..
                            ..
                        END

                    Would add (prefix) 12345-1- to all NATL numbers not
                    otherwise translated. It would add (prefix) 00 to all
                    INTL numbers not otherwise translated.

                        DIAL    /2222 00/1111
                            ..
                            ..
                        END

                    Would append (suffix) 2222 to all NATL numbers not
                    otherwise translated. It would add (prefix) 00 and append
                    (suffix) 1111 to all INTL numbers not otherwise
                    translated.

                    The translation values (strings) does not have to contain
                    number characters (0-9,.-). They can include commands
                    such as "S25=100" etc. as long as your modem supports it.








                                          33




                    COST <NATL COST> <INTL COST>

                    Indicates the start of the cost table. The two (default)
                    parameters are NOT optional. The default cost only
                    applies to numbers with no matching entry in the cost
                    table.

                        COST    5 125           ; NATL default=5, INTL=175
                            1-          75      ; Canada and the US
                            1-808-      125     ; Hawaii
                            46-         27      ; Sweden
                        END

                    An additional parameter can be added after the cost for a
                    number entry indicating the maximum baud rate used. This
                    is useful when calling locations with a lot of line noise
                    etc. Please note that this does not work with several
                    high-speed modems such as the US Robotics Courier HST.
                    You cannot force a HST modem to connect at 2400 with
                    another HST modem by changing the baud rate.

            To compile your nodelist, type FDNC and press <Enter>, or invoke
            the nodelist compiler from FD's main menu, <Alt-N>.

            When FDNC is started, it will compare the date of the raw
            nodelist and its index files. If the dates match, and no update
            has been made to FDNODE.CTL, no compilation will be made and the
            program will ask "Nodelist files are up-to-date, compile
            anyway?".

            If you want to force compilation, run FDNC with the -F command
            line switch.


            5.3 Nodelist flags

            Most of the system entries in the nodelist contain one or more
            capability flags to indicate the system's capability. The Editor
            is capable of displaying, and the Mailer and Terminal are capable
            of using, any nodelist flag present in a system's nodelist entry.


            5.4 Command line switches

            /C

            Compile the nodelist if it (or FDNODE.CTL) has been updated since
            the last time it was compiled, otherwise exit directly. This is
            useful for compiling the nodelist in batch files since it avoids
            the "Nodelist files are up-to-date, compile anyway?" prompt.

            /F

            Forces FDNC to compile the nodelist regardless of whether or not
            it has been updated.



                                          34




            5.5 Points

            As mentioned before, a point is similar to a user logging on to a
            BBS system using his/her terminal program, with the main
            difference being that a point performs most of his/her activities
            offline and use smart software to collect and transit his/her
            mail.

            A point system is addressed by specifying the BOSS system's
            address followed by the point number. E.g. 2:270/17.1 is point
            one of 2:270/17. The BOSS system is called point zero
            (2:270/17.0), but the .0 is normally left out.

            FrontDoor is a point smart software package and fully supports
            the "four-dimensional" (zone, net, node, point) addressing
            method. FrontDoor also supports the "two-dimensional" point
            approach used by some software. This is often called the
            "fakenet" or "pointnet" method. "Fake" because the software uses
            a non-existent network number to identify its "pointnet" and uses
            the node field for the point number.

            The maximum number of points any system can have is 65,535, not
            counting the BOSS, or point zero.


                5.5.1 Pointlist

                A pointlist is similar to a normal nodelist, with the
                exception that all entries are considered point systems.
                FrontDoor, by default, uses the file FDPOINT.PVT to store its
                pointlist. It is possible to add points of other systems to
                your pointlist. This will allow you to enter messages to
                other systems' points just like you would to any other
                system.

                Here is a sample FDPOINT.PVT:

                    ,1,FrontDoor_Development,Strassen,JoHo,-Unpublished-,9600
                    ,2,APX_Development,Strassen,JoHo_Too,-Unpublished-,9600

                As you can see, a point list looks very much like a raw
                nodelist. The last field contains nodelist flags (HST, MO,
                CM, etc.) and if more than one flag is present, they are
                separated by commas.

                Points can also be added to systems in the master nodelist by
                using the POINT keyword:

                ,7,SuperMail_HQ,Strassen_L,Jon_Doe,352-123-456,9600,CM,XA,ZYX
                Point,1,Marketing,Strassen,Jon's_Uncle,-Unpublished-,9600
                ,17,UseMail_HQ,Strassen_L,Jill_Doe,352-234-567,9600,CM,XA,HST
                Point,1,The_Lab,Strassen_L,Jill's_Uncle,-Unpublished-,9600

                Assuming this was listed under the Net-270 host in zone two,
                we have created 2:270/7, 2:270/7.1, 2:270/17, and 2:270/17.1.



                                          35




                The second example works well if your nodelist is not updated
                frequently (weekly, daily, etc). But if you have to add the
                "Point,#" every time you get a new nodelist, this task
                becomes rather tedious.

                FrontDoor therefore supports an additional pointlist format:

                Boss,2:270/7
                ,1,Marketing,Strassen,Jon's_Uncle,-Unpublished-,9600
                Boss,2:270/17
                ,1,The_Lab,Strassen_L,Jill's_Uncle,-Unpublished-,9600

                This does away with the need to constantly update the BOSS
                system's data in the raw nodelist and allows you to put your
                pointlist in a separate file. FDNC will then take the BOSS
                system's data from the master nodelist.


                5.5.2 FDNODE.CTL

                If you only have one file with point definitions, you can put
                them in FDPOINT.PVT and use the third example (above) to add
                points for other systems, or your own system. If you have
                more than one file with point definitions, however, you
                should NOT name any of them FDPOINT.PVT.

                Assume we have two files with pointlists:

                    FDHQ.PTS:

                    ;
                    ;   Pointlist for 2:270/17
                    ;
                    Boss,2:270/17
                    ,1,The_Lab,Strassen_L,Jill's_Uncle,-Unpublished-,9600
                    ,2,The_Office,Strassen_L,Jill's_Sister,-Unpublished-,9600

                    and

                    WIZOZ.PTS:

                    ;
                    ;   Pointlist for 1:135/990
                    ;
                    Boss,1:135/990
                    ,1,OZ_Point,Miami_FL,Dorothy,-Unpublished-,9600

                We would tell FDNC to merge these two files into FDPOINT.PVT
                before it compiles the nodelist, by specifying the following
                in FDNODE.CTL:

                    pointlist   C:\FD\NODELIST\WIZOZ.PTS
                    pointlist   C:\FD\NODELIST\FDHQ.PTS





                                          36




                The BOSS statement in FDHQ.PTS and WIZOZ.PTS can be removed
                if you instead specify:

                    pointlist   C:\FD\NODELIST\WIZOZ.PTS    1:135/990
                    pointlist   C:\FD\NODELIST\FDHQ.PTS     2:270/17

                You must ALWAYS specify the address of the BOSS system (as
                shown above) if it is not listed in the actual pointlist
                file.


                5.5.3 Treatment of points

                A point system is treated just like any other system with one
                exception. A point system of another system than your own is
                always treated as its BOSS (or point zero) system. When the
                Mailer creates mail packets for 1:135/990, it includes mail
                for any points under it by default.


                5.5.4 Remapping

                If you have points that uses "point dumb" software, ie. which
                does not support the "four dimensional" (zone, net, node,
                point) concept fully, you must tell FrontDoor about this.
                Since FrontDoor supports the "four dimensional" concept, it
                has to remap mail from and to "point dumb" software.


                5.5.5 POINTNET

                If the POINTNET environment variable is set, mail from and to
                systems with the same net number as the value of POINTNET is
                remapped.

                    E.g. in AUTOEXEC.BAT:

                        SET POINTNET=1004

                Would force FrontDoor to remap mail from and to 1004/1,
                1004/2, 1004/3, and 1004/4 to 2:270/17.1, 2:270/17.2,
                2:270/17.3, and 2:270/17.4 respectively; assuming your
                network address is 2:270/17.

                FrontDoor automatically remaps messages that it extracts from
                mail packets. If you use the POINTNET variable, FrontDoor
                will treat 1004/1 identical to 2:270/17.1; assuming your
                network address is 2:270/17.










                                          37




            5.6 Sharing the nodelist

            FrontDoor is capable of using the nodelist together with another
            program that supports sharing of the nodelist. If you are running
            FrontDoor under DESQview or LANtastic, for example, it is
            possible to run the Mailer at the same time as the Editor,
            sharing the same nodelist.

            When FDNC compiles the nodelist, you must, however, make sure
            that no other program (including text editors) is using any of
            the nodelist files (FDPOINT.PVT, FDNET.PVT, and/or the raw
            nodelist).


        6 Modems and FOSSIL drivers

        FrontDoor works with most "Hayes-compatible" modems, including US
        Robotics HST and HST/DS, Telebit's Trailblazer, ANC, Everex, ZyXEL
        and Hayes. The general rule is that the modem must be able to send
        alphanumeric result strings. For most low-speed modems, the basic
        configuration is all that is required. For high-speed modems such as
        the US Robotics HST, a few extra settings are necessary.

        To utilize high-speed modems in the most efficient way, it must be
        properly configured for use with FrontDoor. Some high-speed modems
        are incorrectly configured for use with FrontDoor when they leave
        their factory.

        FrontDoor require that your modem can return verbal result codes,
        such as "CONNECT 2400" and "NO CARRIER". In addition, if you want
        FrontDoor to answer the telephone on inbound calls, the modem must be
        able to return a verbal code indicating a ring signal, such as
        "RING". The modem must not have DCD (carrier detect) forced. It
        should support disconnecting by lowering DTR (data terminal ready),
        but it is not necessary. DTR must, however, not be forced.

        For high-speed modem users, it is usually recommended that you lock
        the DTE (computer<>modem) speed to the highest possible baudrate;
        which is usually 19200, 38400, or 57600 BPS.

        The current version of FrontDoor does not support manually operated
        modems with constant DTE speeds since most of them do not send any
        type of messages to the terminal (program). This is expected to be
        implemented in future versions.


            6.1 Basic configuration

            The modem options are located in FDSETUP under the MODEM >
            Default settings pull-down menu. There are four sub-menus,
            Hardware, Messages, Command strings, and Answer control.

            Hardware

            The Hardware option screen allows you to configure things like
            the highest baudrate supported by your modem, the COM port to
            which your modem is connected, etc.

                                          38




                Serial port

                The COM port your modem is attached to (1-32).

                Locked port

                Whether or not you have locked the FOSSIL driver's baudrate.

                Maximum baudrate

                The maximum supported baud rate of your modem (300-38400
                BPS). If you have locked your FOSSIL driver (discussed
                later), set this to 38400 BPS.

                Reset modem to connect speed

                >>> This option should ONLY be used if you have a modem that
                    supports the CCITT V.23 (split speed, 1200/75 and
                    75/1200) recommendation.

                Lower DTR when busy

                Determines how the Mailer should handle the modem when it
                invokes other programs, exits, and shells to DOS. If enabled,
                the Mailer will simply lower DTR. This means that your modem
                will not answer the phone, but any calling systems will not
                get a busy signal. If you disable this, the Mailer will send
                the Offhook string to the modem instead of lowering DTR. This
                can be used to take the modem offhook when your system is not
                available so that calling systems gets a busy signal instead
                of no answer.

                >>> It is against the law of some countries to take a modem
                    offhook unless actual communication is taken place. As
                    the operator of FrontDoor, it is your responsibility to
                    be aware of such laws in your own country.

                Lower DTR to terminate call

                If enabled, the Mailer will drop DTR for a short period of
                time to terminate calls. Most modems supports this and you
                should only disable it if your modem does not support
                lowering of DTR. If disabled, the Mailer will send the Escape
                code string followed by the Onhook string to terminate a
                call.

                Toggle DTR before dialing

                Specifies that the Mailer should lower DTR, pause, and then
                raise DTR again every time it places an outgoing call. While
                this increases the chances of call collision, it may be
                required by some modems to reset properly, etc. Do not enable
                this option unless it is absolutely necessary.





                                          39




        <C>     Carrier detect mask (CDMASK)

                The bitmask the Mailer should use when asking the FOSSIL
                driver for the port status to determine if a carrier signal
                is still present.

            Connect messages
            Status messages

            These options allows you to define the messages sent by your
            modem. If your modem does not send one or more of the strings you
            should NOT remove them.

            The 300 string is sent as CONNECT followed by a carriage return
            by some modems (US Robotics HST for example). You should
            therefore set the string to CONNECT| (the pipe character will be
            replaced with a CR by the Mailer) if this is the case with your
            modem.

            The RING string should be set to RING| (the pipe character will
            be replaced with a CR by the Mailer) if your modem sends the
            RINGING message while waiting for a call to be connected.

        <+> Custom message

            Allows you to define a custom connect message and its associated
            baudrate in the event that your modem returns a connect message
            not otherwise covered by FrontDoor; such as "CONNECT FAST".

            Command strings

            All command strings may contain a pipe (|) character, which
            translates into a CR and a tilde (~) character which translates
            into a one second pause.

                Escape code

                Used to place the modem in command mode (as opposed to data
                mode). This is only used if you have disabled Hardware >
                Lower DTR to terminate call or if you are using the Hardware
                > Reset modem to connect speed option.

                Return on-line

                Used to place the modem in data mode (as opposed to command
                mode). This is only used if you are using the Hardware >
                Reset modem to connect speed option.

                Onhook

                Used to place the modem on-hook (as opposed to off-hook) if
                you have disabled Hardware > Lower DTR when busy or Hardware
                > Lower DTR to terminate call".





                                          40




                Offhook

                Used to place the modem off-hook (as opposed to on-hook) if
                you have disabled Hardware > Lower DTR when busy.

                Dial

                Used when the Mailer places an outgoing call. The Mailer will
                send the dial (this) string, the Prefix, the telephone
                number, followed by the Suffix.

                    I.e. <Dial><Prefix><Number><Suffix>

                Prefix

                Sent before every number when the Mailer places an outgoing
                call (see above).

                Suffix

                Sent after every number when the Mailer places an outgoing
                call (see above). This should be set to the pipe (|)
                character to indicate a CR in most cases.

                Delay

                The delay (in 1/10 second) between every string the Mailer
                sends to the modem. If you have a mode that accept commands
                rapidly, such as the US Robotics HST, you can set this as low
                as one or two, but most modems require that this is set
                between four and eight.

                Init-1..Init-3

                Modem initialization strings. They are sent every time the
                Mailer initializes the modem in order (Init-1, Init-2,
                Init-3). Unused strings should not be set to anything (leave
                field blank).

                Down

                Sent to the modem when the Mailer terminates. This occurs
                when mail has been received or when the Mailer terminates
                execution.

                Reset

                Sent to the modem to force it to respond with an OK message.
                This should be set to "AT|" in most cases.









                                          41




            Answer control

                Manual answer

                Specifies that the Mailer should wait for the RING message
                from the modem and then send the force answer string (below)
                to force the modem to answer.

                >>> This is the safest way to control modem answering and
                    should be used unless your modem does not support it. For
                    Hayes compatible modems, you should add S0=0 to one of
                    your init strings to prevent the modem from answering
                    automatically.

                Force answer

                The string forcing the modem to answer an incoming call. This
                should be "ATA|" in most cases.

                Answer delay

                When the Mailer receives the RING message from the modem, it
                will pause for nn 1/10 seconds before sending the force
                answer string. This should be set between four and eight for
                most modems.

        <+>     Enable LDFRS

                Enables Logging of Data Following Ring Signal (DFRS). This is
                mainly used in areas that offer CALLER*ID as a service to
                their subscribers. The CALLER*ID data will be logged between
                the first and the second RING in most cases.

        <C> Fax

            Used to enable or disable the internal Fax handling of the
            Mailer.


            6.2 Advanced configuration

            Many modems have several different connection modes and options.
            The US Robotics HST/DS, for example, can be configured between
            several different connect modes, including CCITT V.32, CCITT
            V.32bis, and the proprietary HST protocol.

            Since the nodelist normally indicates a system's hardware (modem)
            capabilities, the Mailer can automatically reconfigure your modem
            depending on what type of hardware the remote system being called
            is using. This automatic reconfiguration feature can also be used
            to disable or enabled certain options for specific systems (i,e.
            not based on nodelist data) because of problems with noisy lines,
            long satellite delays, etc.

            This is all configured in the MODEM MANAGER under the Manager
            pull-down menu in FDSETUP. The actual data is stored in a file
            called MODEM.FD in the SYSTEM directory.

                                          42




            6.3 The Modem Manager

            The entries are processed as defined, i.e. in sequential order,
            top to bottom. It may be important in which order these options
            are configured and triggered, the modem manager therefore allows
            you to re-arrange individual entries by using the Move (F2)
            option.

                String to match

                A nodelist flag, such as HST, a baudrate, such as 2400, or a
                complete network address, such as 2:270/17, that the Mailer
                should match in order to send the specified string. To
                specify a baudrate, place it behind an equal sign, e.g.
                =2400.

                >>> The Mailer supports any ASCII text to be entered as the
                    String to match. The data you enter is matched verbatim
                    with the data in the nodelist. It is for this reason that
                    the FidoNet user (U) flag must be taken into
                    consideration. I.e. "ISDN" does not match "UISDN", nor
                    does "UISDN" match "ISDN".

                String to send

                The string that will be transmitted to the modem when a match
                is made. The pipe (|) character is translated to a CR and
                should terminate the string in most cases.

            The Mailer will ignore entries with INACTIVE status.

            An example, the HST/DS

            Most HST/DS owners will have the following three lines at the
            beginning of their MODEM MANAGER list:

                V32         ATB0|
                HST         ATB1|
                V32B        ATB0|

            The first line, V32, will transmit "ATB0" followed by CR to the
            modem if the system to be dialed has V32 in its nodelist flags.
            This is to enable the HST/DS' CCITT V.32 handshake.

            The second line, HST, will transmit "ATB1" followed by a CR to
            the modem if the system to be dialed has HST in its nodelist
            flags. This is to tell the modem that we prefer the HST protocol.
            In the case of a system with both the V32 and the HST flag, we
            want the HST flag, because that protocol is faster than the CCITT
            V.32 protocol.

            The third line, V32B, will transmit "ATB0" to the modem if the
            system to be dialed has V32B in its nodelist flags. This it to
            tell the modem that we prefer the CCITT V.32bis protocol. In the
            case of a system with both the V32B and the HST flag, we want the
            V32B flag.


                                          43




            Let us assume our modem has a problem, with incorrect busy and
            voice signal detection, when it encounters a modem that answers
            using the PEP protocol handshake (used by Telebit Trailblazers
            for example), we would then want to disable our modem's
            capability to detect a busy signal and/or a voice signal. We
            would then add:

                PEP     ATX2|


            6.4 FOSSIL drivers

            A FOSSIL (Fido/Opus/SEAdog Standard Interface Layer) driver is a
            memory resident program (TSR) that works as a layer between the
            application program and your computer's hardware. The Mailer
            requires a FOSSIL driver to function. One of the advantages of
            the standard FOSSIL interface is that programs can be ported
            easily to other machines and/or operating systems, or to
            communicate with devices that do not normally function like a
            "Hayes compatible" modem, such as ISDN cards.

            There are several FOSSIL drivers available. The Mailer has been
            tested with OpusComm, X00, and BNU with good results. X00 and BNU
            will be described here.

            BNU

            BNU, written by David Nugent, comes in two flavors. One is a
            device driver, the other is a .COM file, loaded from AUTOEXEC.BAT
            or another batch file. The .COM flavor is assumed in the example.
            For a detailed description of the BNU driver, please refer to the
            documentation included in the BNU distribution archive.

                [AUTOEXEC.BAT]

                BNU /R=1024 /T=512 /L1:57600

                /R=1024

                Specifies a receive buffer of 1024 bytes.

                /T=512

                Specifies a transmit buffer of 512 bytes.

                /L1:38400

                Locks COM2 at 57600 BPS (for use with a high-speed modem such
                as the ZyXEL U1496-E+).

                If you are not using a high-speed modem the above example
                should most likely be modified to not lock COM2.






                                          44




            X00

            X00, written by Ray Gwinn, is a device driver (later versions can
            also be loaded as an executable from AUTOEXEC.BAT), it is loaded
            from your CONFIG.SYS file when your machine is started. For a
            detailed description of the X00 driver, read the documentation
            included in the X00 distribution archive.

                [CONFIG.SYS]

                device=X00.SYS E 1 B,1,57600 T=512 R=1024

                    E

                    Disable 5 second advertisement when X00 is first loaded.

                    1

                    Number of COM ports X00 should allow to be accessed at
                    one time.

                    B,1,57600

                    Locks COM2 at 57600 BPS.

                    T=512

                    Specifies a transmit buffer of 512 bytes.

                    R=1024

                    Specifies a receive buffer of 1024 bytes.

                If you are not using a high-speed modem the above example may
                not be what you want. The most common command line for X00
                is:

                    device=X00.SYS E 1

            OS/2 2.x

            FrontDoor can be used in an OS/2 DOS box with excellent results.
            The two drivers described above, BNU and X00, should, however,
            not be used for optimum results. Two drivers that have been
            tested with good results exist. The first one, VFD for Virtual
            FOSSIL Driver, written by Joakim Hernberg is a FOSSIL layer that
            interfaces with the native OS/2 2.x COM driver (or compatible
            replacements thereof); the other is SIO/VX00 by Ray Gwinn.

            A separate FrontDoor Technical Note (FDTN), number two (2), can
            be found on many systems that describe the exact details of how
            to add these drivers to your OS/2 configuration.






                                          45




        7 Events

        There are two basic types of events. Mail events and external events.
        Mail events are used to control how the Mailer treats mail during a
        given time of the day. External events are used to force the Mailer
        to terminate with an errorlevel at a specific time. They can be used
        to run system maintenance programs, disk optimizers, etc.

        The EVENT MANAGER in FDSETUP is used to control mail and external
        events. There is a (required) global event, which is active when no
        other event is active. The @ character is used for the global event.


            7.1 The Event Manager

            The event manager has two modes. The first is the view mode,
            which is self explanatory. The second mode is the edit/create
            mode. It will now be described.

                Tag (T)

                The event ID. A letter from A-Z or @. The @ event has special
                meaning and is described later. X is used for eXternal
                events, all other letters are used for mail events. Which
                letter you use is not important. They could correspond with
                the time of day, N for Night, E for Evening, D for Day, etc.
                The event tag is used to associate an event with a schedule
                block in the route file (see "Mail routing").

                Days

                The days you want the event to be active on. The @ event is
                active on all days.

                Modifier (M)

                You can define a start time for the @ event. It is not used
                to control the start of the @ event. It can be added,
                subtracted, or ignored, when calculating the actual start
                time of other events.

                If the modifier for an event is +, the start time of the @
                event is added to the start time of the event.

                If the modifier for an event is -, the start time of the @
                event is subtracted from the start time of the event.

                If the modifier for an event is *, the start time of the @
                event is ignored and not used to calculate the actual start
                time of the event.

                This is useful when it is time to switch between winter and
                summer time. Instead of having to manually go into each event
                and define a new start time, you could change the start time
                of the @ event and the start time of all other events will be
                changed.


                                          46




                Let us assume that you have an event (tag=E) that starts at
                08:00 in the morning with a modifier of +. Your @ event has a
                start time of 01:00. Since the modifier was + (add), the
                start time of @ (01:00) will be added to the start time of
                the E event and the result will be that event E starts at
                09:00. If you change the modifier to - (subtract), the start
                time of event E will be 07:00 (08:00 minus 01:00). If you set
                the modifier to * (ignore), the start time of E is not
                affected.

                Start time

                Defines the start time of an event. See Modifier (above) for
                an explanation on how this can be affected.

                Length

                Defines the length of the event. External events (X) always
                have a length of 00:01 (one minute).

                Errorlevel

                For external (X) events, this defines the errorlevel that the
                Mailer will terminate with. For mail events, this defines the
                errorlevel to exit with if mail is received (and the Mailer
                is triggered to exit). If the errorlevel field is set to
                zero, the default Mailer > Errorlevels > MAIL RECEIVED
                errorlevel will be used.

                You may use any value in the range 31-255.

                Min.cost

                Defines the minimum cost of messages that should be qualified
                (see "Mail routing").

                Max.cost

                Defines the maximum cost of messages that should be qualified
                (see Mail Routing). A value of -1 forces the Mailer to ignore
                the cost of messages.

                Behavior

                Defines the behavior of the event. Mail events and eXternal
                events have different behavior options, this is described
                later.

                Retry delay

                Defines the delay (in seconds) the Mailer should wait between
                placing outgoing calls. A value of zero means that you want
                the Mailer to use the default delay (described above).





                                          47




                7.1.1 External event behavior

                Allow users during event

                Defines whether or not non-mail (human) calls are allowed to
                interrupt the event.

                If a non-mail call comes in at 12:00 and you have an external
                (X) event scheduled for 12:30, the Mailer will take the X
                event into account when calculating the number of minutes
                left until the next event, depending on how this option is
                set. If it is disabled, the user would, in this case, only
                have 30 minutes until the next event. If it was enabled, the
                Mailer would instead scan ahead for the next (if any) event
                that does not allow users.

                Forced

                Defines whether or not the event is forced. The Mailer, by
                default, ignores events that it "missed" while doing
                something else. If you enable this option, the event will be
                executed even if the Mailer have "missed" it.

                Assume you have a non-forced external (X) event scheduled for
                12:00 and a user calls in at 11:50. The call lasts for 30
                minutes (12:20). When the Mailer is brought back up again,
                the external event will not be executed. If, however, you had
                this option enabled for the external (X) event, it would be
                executed as soon as the Mailer was brought up again.

                Inactive

                Toggles the state of the event. The Mailer will ignore any
                inactive events. This allows you to deactivate events without
                removing them from the event manager.


                7.1.2 Mail event behavior

                Allow users during event

                This has the same function as for eXternal events. In
                addition, if this option is set to "NO" (disabled),
                interactive (non-mail) calls will not be accepted during the
                duration of the event.

                Exit when mail is received

                Defines whether or not you want the Mailer to exit when mail
                has been received. This allows you to process received
                echomail, etc.

                High priority (crash) mail only

                Forces the Mailer to ignore messages that does not have crash
                status. Note that messages with IMM (Immediate) status are
                not affected by this.

                                          48




                Allow file requests

                Defines whether or not you want the Mailer to honor file
                requests during an event. If you disable this option, the
                Mailer will simply ignore file requests.

                Pickup file requests

                The Mailer will by default not accept file requests received
                during an outgoing (outbound) mail call since you are paying
                for the call. This option allows you to pickup waiting file
                requests and process them. Whether or not they are actually
                honored is defined by the Allow file requests option.

                Hold (do not send) file requests

                Forces the Mailer to ignore outgoing (your own) file request
                messages during the event. This is useful if you do not want
                to send out file requests during daytime events for example.

                Hold (do not send) file attaches

                Forces the Mailer to ignore outgoing (your own) file attach
                messages during the event. This is useful if you do not want
                to send out files attached to messages during daytime events
                for example.

                Attempt to pickup waiting mail

                Defines whether or not you want the Mailer to pickup any
                waiting mail on outgoing calls. The default (YES) should be
                used unless you want the Mailer to terminate the mail session
                as soon as it has delivered its mail. If this option is
                disabled, your file requests (if any) will fail since the
                Mailer terminates the call before the remote system has a
                chance to process them.

                Allow nodes to pickup waiting mail

                This option is the same as using the DENY route command (see
                "Mail routing"). The only difference is that you cannot be
                selective about which systems can pickup waiting mail. If a
                system calls in to deliver its mail and this option is
                disabled (NO), your system will not release (send) any
                waiting mail.

                Prioritize outbound calls

                Forces the Mailer to make outgoing calls without waiting for
                the specified time (retry delay) between calls. The Mailer
                will still accept incoming (inbound) mail, but the chances of
                another system getting through are very small.

                Inbound-Only

                Specifies that you do not want the Mailer to make any
                outgoing calls during the event.

                                          49




                End event when no more mail to send

                If you have an event with some restrictions on other systems
                or do not allow users, it may be useful to enable this
                option, forcing the Mailer to release all restrictions
                enforced by the event as soon as there is no more mail to
                send.

                If new mail is entered that qualifies for mailing and the
                event has ended (prematurely), it will be restarted.

                Send to CM systems only

                Forces the Mailer to only qualify those systems that have the
                CM (continuous mail) flag set in their nodelist entry.

                Send to non-CM systems only

                Forces the Mailer to only qualify those systems that Do not
                have the CM (continuous mail) flag set in their nodelist
                entry.

                Send to systems once only

                Forces the Mailer to only deliver mail to a system once
                during the event. If the event is interrupted or aborted, the
                Mailer will remember which systems it has already delivered
                mail to and when the event is restarted, it will not call
                those systems again.

                Assume you have mail to 1:135/20 and 2:310/11 during event A,
                with this behavior enabled. On the first call to 1:135/20,
                the Mailer sends its mail successfully. If the event is
                restarted for some reason (user break, human caller, mail
                received exit), the Mailer will not call 1:135/20 again, even
                if there is new mail for that system.

                Answer inbound calls

                If you have specified that you want the Mailer to force the
                modem to answer when it receives a RING message (see Modem >
                Answer control), this setting ultimately determines whether
                or not the Force answer string is sent to the modem, or if
                the Mailer should simply ignore the RING message. This allows
                you to control when the Mailer should answer inbound calls.

                Inactive

                The same as for eXternal events.


                7.1.3 The @ event

                The @ event is active whenever your system is not in another
                mail event. The @ event is required. You do not have to tell
                the Mailer to send mail during the @ event, but it must be
                defined.

                                          50




                You can use it to send local and/or low cost mail whenever
                the Mailer is not busy, etc. You can specify a schedule block
                (see Mail routing), using the @ tag and define routing rules
                for it just like any other mail event. If the Mailer does not
                find a schedule block for the @ tag, it will still use any
                global rules defined in the route file.


                7.1.4 Overlapping events

                Overlapping events are fully supported by the Mailer.

                Event B starts at 05:00 with a duration of 01:00. Event A
                starts at 05:01 with a duration of 00:15. The behavior for
                event A includes Only execute event once and End event when
                no more mail to send.

                Event B will start at 05:00, after one minute, event A will
                start and last for fifteen minutes (or end when there is no
                more mail to send).

                Once event A has ended, B will resume. This is a very
                powerful and useful concept. It can be used to start
                temporary or dynamic events within events that lasts for
                several hours.


        8 Mailer

        The Mailer is the core program of FrontDoor. It is responsible for
        sending and receiving messages and files; and optionally pass human
        callers to a BBS or other interactive software. The Terminal function
        is also located in the executable file of the Mailer and can be
        reached from one of its menus.

        Most functions of the Mailer are reached by holding down the <Alt>
        key and pressing a key, A through Z.


            8.1 Menus

            Each function and menu of the Mailer will now be described.


                8.1.1 Programs      <Alt-P>

                Message Editor      <Alt-E>

                Loads the message Editor.

                Terminal            <Alt-J>

                Invokes the Terminal (it resides in the Mailer's overlay
                file, FD.OVR).




                                          51




                Configure           <Alt-C>

                Loads the configuration program, FDSETUP.

                Nodelist            <Alt-N>

                Loads the nodelist compiler, FDNC.

                User keys           <Alt-K>

                Displays the 20 (24) user definable function keys and allows
                you to select one.

                DOS shell           <Alt-Z>

                Invokes a temporary DOS shell. Type EXIT and press <Enter> to
                return to the Mailer. Packets created with any of the
                temporary mail services function (File Request, Transmit
                file, Send mail) will be discarded when you return and the
                Mailer will rescan the contents of the NetMail folder.

                Quit                <Alt-Q>

                Returns you to DOS or the batch file that first executed the
                Mailer. The Mailer will return errorlevel 10 (User Break).


                8.1.2 Utilities     <Alt-U>

                Active event        <Alt-A>

                Displays the settings for the currently active event.

                Inbound history     <Alt-I>

                Invokes the inbound call (mail) history management function.

                Outbound history    <Alt-O>

                Invokes the outbound call (mail) history management function.

                Recent activity     <Alt-R>

                Shows you the last two days of general activity, failed
                sessions, file requests, number of files/bytes sent and
                received, etc.

                Disconnect          <Alt-X>

                Allows you to manually terminate a call. This will also
                re-initialize the modem.

                Lock keyboard       <Alt-L>

                Allows you to lock the keyboard (and the Mailer) against
                unauthorized use. The Mailer will still perform its duties
                such as sending and receiving mail, etc.

                                          52




                You must enter the specified password to unlock the keyboard.
                If the Mailer exits (due to mail received or an interactive
                call is received), the keyboard lock status is retained and
                when the Mailer is restarted, the keyboard will remain
                locked.

                Restart event       <Alt-F7>

                Forces the Mailer to rescan the message base and create new
                mail packets. All previous temporary packet information is
                discarded.


                8.1.3 Mail          <Alt-M>

                Queue manager       <Alt-B>

                Allows you to manipulate the current mail queue. If no mail
                event is active, the mail queue is empty. The mail queue is
                described in a separate section.

                Undialable manager  <Alt-V>

                Allows you to manipulate systems marked as undialable. This
                is discussed in a separate section.

                Forced poll         <Alt-F>

                Creates a priority entry in the mail queue for the specified
                system. If an entry for the specified system already exists
                in the queue, its status is set to priority.

                >>> If the Mailer has to rescan the message base, the
                    temporary poll is removed from the mail queue.

                Request files       <Alt-G>

                Allows you to create a temporary file request to the
                specified system.

                >>> If the Mailer has to rescan the message base, the
                    temporary file request is removed from the mail queue.

                Transmit files      <Alt-T>

                Allows you to transmit files to the specified system. As with
                the poll and request function (above), this is only a
                temporary function.

                >>> If the Mailer has to rescan the message base, the entry
                    is removed from the mail queue.







                                          53




                Send mail           <Alt-S>

                Allows you to create a temporary mail packet for the
                specified system. You can choose to include all or
                high-priority mail.

                >>> If the Mailer has to rescan the message base, the entry
                    is removed from the mail queue.


                8.1.4 Your profile      <Alt-Y>

                    Answer

                    Allows you to toggle the manual answer status. This
                    option is only valid if you have enabled the manual
                    answer option in FDSETUP. Note that if you manually
                    toggle this option, the Mailer will honor the new setting
                    until it exits.

        <C>         Printer

                    Allows you to toggle the printing of new (incoming)
                    messages.

                    Human callers

                    Allows you to toggle whether or not you want the Mailer
                    to accept human callers. This option is only valid if you
                    are not running FD in mail-only mode.

                    Exit on mail

                    Allows you to toggle whether or not the Mailer should
                    exit when mail has been received. This option is only
                    valid if an errorlevel for received mail has been
                    specified in FDSETUP and the active event (if any)
                    specifies that the Mailer should exit when mail has been
                    received.

                    Which AKA       <Alt-W>

                    Allows you to select a different AKA to operate under.
                    The specified AKA will be active until the Mailer exits
                    or you select a new AKA to operate under. Note that this
                    does not effect the AKA matching function of the Mailer.


            8.2 Mail queue      <Alt-B>

            The mail queue function allows you to modify the status of one or
            more mail packets, temporarily change the destination of mail
            packets, and to unpack one or more packets.





                                          54




            Priority            <F1>

            Sets priority status on all selected packets. Packets with
            priority status are always processed before packets with crash or
            normal status.

            Verbose             <F2> or <Enter>

            Displays more information about the highlighted mail packet such
            as attached files, estimated transfer time, etc.

            Crash               <F3>

            Sets crash status on all selected packets.

            Hold                <F4>

            Sets hold status on all selected packets. Packets with hold
            status will never be sent by the Mailer unless the destination
            system calls in to pickup mail.

            Select all          <F5>

            Toggles the selected status for all packets.

            Destination         <F6>

            Changes the destination of all selected packets. When the Mailer
            processes the mail queue, it will treat all active (non-sent and
            non-held) packets as individual packets, including two or more
            different packets destined for the same system. If a connection
            is made (whether the destination system calls you or your system
            calls it), however, all packets destined for that system will be
            sent.

            Unpack              <F7>
            Discards all selected packets from the queue. This will not
            delete any mail from the NetMail folder.

            Clear status        <F8>

            Sets normal status on all selected packets.

            Clear busy retries  <F9>

            Sets the dial attempts for all selected packets to zero.

            Exit                <Esc>

            Returns you to the Mailer's main screen.

            Select              <Space>
            Toggles the selected status of the currently highlighted packet.





                                          55




            8.3 Call progress

            When the Mailer has mail to send, it will step through the mail
            queue and call the systems with mail packets waiting. Packets
            with sent, failed, and hold status are ignored. These can,
            however, always be picked up by the destination system if it
            calls in.

            After every unsuccessful (BUSY, NO CARRIER, etc.) call, the busy
            retry counter is incremented until it reaches the value defined
            in FDSETUP. Once the limit has been exceeded, the Mailer puts
            hold status on the packet. If a connection is made but the actual
            transfer fails, the resend retry counter is updated and once the
            limit, defined in FDSETUP, is reached, the packet receives failed
            status.

            Press <Space> to force the Mailer to place the next outgoing
            call.


            8.4 Semaphore indicators

            Every time the Mailer scans the NetMail folder, it looks for
            unread messages destined for your system. If any are found, it
            will enable the flashing "Mail" text in the bottom right hand
            corner. Once the message(s) have been marked received (read), the
            flashing mail text will disappear.


            8.5 Undialable

            When the Mailer reaches the resend (session failure, transmission
            failure, etc.) retry limit for a system during an event. That
            system is added to the undialable table with a "grade" of one.
            When the "grade" reaches three, the system is considered
            undialable and will never be called again (until you manually
            "upgrade" it).

            The undialable manager is accessed by pressing <Alt-V> from the
            Mailer's main menu and allows you to "upgrade" a system's status,
            add a system manually to the undialable list, and remove one or
            more undialable systems.

            The undialable system information is kept in NODIAL.FD in
            FrontDoor's SYSTEM directory.


        9 Editor

        The Editor is the program used to write and read messages. It can be
        invoked from the command line in DOS by typing FM followed by
        <Enter>, or from the Mailer by pressing <Alt-E>.

        The Editor has two "status" lines. The bottom status line is used to
        display the current message, number of messages in the current
        folder, the lowest and highest message numbers and the number of
        messages remaining to the last message (last minus current).

                                          56




        The top status line shows the currently active AKA (address), the
        current time and the folder you are in.

        Most functions of the Editor are reached by holding down either the
        <Ctrl> or <Alt> key and pressing a key, A through Z. If you press a
        key that has no function assigned to it, it will display a message
        saying "Press Alt-H for help" on the bottom status line.

        Each function and menu of the Editor will now be described.


            9.1 Main            <Alt-M>

            Create              <Ins>

            Allows you to create a new message in the current folder. You
            will be prompted for the destination (user name and possibly a
            network address), subject, etc.

            Delete              <Del>

            Removes the currently displayed message. The Editor will ask you
            to confirm that you really want to remove the message.

            Reply               <Alt-R>

            Similar to the Create function. The destination of the newly
            created message, however, is taken from the sender of the message
            you are replying to. This function also allows you to quote the
            original message, in whole, or selected parts.

            NetMail reply       <Alt-N>

            Similar to the Reply function. If you are in a Local or
            Conference folder, your message (the reply) will be placed into
            the NetMail folder. The destination address of the message is
            taken from either the origin line (Conference folders) or the
            sender's name (Local folders).


        <C> Reply comment       <n/a>

            Similar to the Reply function. It allows you to create a
            follow-up message with additional comments to the same
            destination as the original message.

            Forward             <Alt-L> or <Tab>

            This function allows you to redirect a message to someone else.
            It will also insert some additional information at the top of the
            redirected message, indicating who the message was originally
            from, etc. You can choose whether or not you want to overwrite
            the original message with the forwarded (redirected) message.

            The Forward function will also add the default message status to
            the message and remove the Rcvd and Sent status bits if they were
            set.

                                          57




        <C> View fax            <n/a>

            Invokes the external fax viewer, allowing you to view documents
            attached to a fax cover page message.

            Folders             <Alt-F>

            Allows you to change the active folder. You cannot change to
            another folder while editing a message, but you can view the
            folder list. The type of each folder is shown as 'E' for
            Conference, 'L' for Local and 'M' for NetMail.

        <C> The commercial version allows you to configure any folder with
            NetMail status, the type will then be displayed as 'N'. The
            shareware version only has one NetMail-type folder.

            To select a folder, you can use the arrow keys to move the
            highlight bar and then press <Enter>, or you can type the number
            of the folder followed by pressing <Enter>.

            Folder scan         <Ctrl-F>

            Scans all folders and indicates which folders have any message
            number higher than the last read message. Typically, this means
            that new messages have arrived in a folder since you last
            accessed it.

            DOS shell           <Alt-Z>

            Invokes a temporary DOS shell. Type EXIT and press <Enter> to
            return to the Editor.

            Leave editor        <Alt-Q>

            Returns you to DOS or to the Mailer, depending on how the Editor
            was invoked. If you are editing a message, you will be asked
            whether or not you wish to save it before exiting.


            9.2 Edit            <Alt-E>

            Status              <Alt-S>

            Allows you to change the status of a message. See the separate
            section about Message Status Bits for a detailed description of
            this.

            Subject             <Alt-A>

            Allows you to change the subject of a message. If you have a
            message with file attaches and press <Alt-A>, the file attach
            list will be processed again and if you specified wild-cards or
            more than one file on the subject line, you will have to select
            the files you want to send once again.




                                          58




            Text                <Alt-T>

            Allows you to edit the text (body) of a message. If you are
            already in editing mode, this will bring up a secondary menu with
            text editing related functions.

            Destination         <Alt-D>

            Allows you to change the destination of a message. This will add
            the default message status bits as well as the Local bit to the
            message and remove the Rcvd and Sent status bits if they were
            set.

            As opposed to the Forward function, using <Alt-D> will not result
            in any text being added to the message body (forwarding info).

            Toggle              <Ctrl-F2>
            Brings up the toggle menu.


                9.2.1 Edit mode <Alt-T>

                Import file     <Alt-F2>

                Allows you to import an ASCII file into the text. The
                contents of the file will be inserted at the current cursor
                position.

                Insert line     <Ctrl-Enter>

                Inserts a blank line after the current line. The cursor will
                remain in the same position.

                Line to buffer  <Ctrl-B>

                Adds the current (where cursor is positioned) line to end of
                the temporary buffer and moves the cursor down one line. The
                last eighty lines of deleted/marked text is always retained
                in a temporary buffer and can be reinserted with <Alt-F1> or
                <Esc>.

                Delete word     <Ctrl-W>

                Deletes the word to the right of the cursor.

                Go to line #    <Ctrl-G>

                Allows you to specify an absolute line number to place the
                cursor on.

                Delete to EOF   <Ctrl-T>

                Deletes all text from cursor to end of message.





                                          59




                Find            <Alt-F5>

                Searches for the specified string, and if found, places the
                cursor on the first character of the found word.

                Find & Replace  <Alt-F6>

                Allows you to replace a string with another. Note that this
                function will restore the cursor position whereas the Find
                function will not.

                Re-format       <Alt-F8>

                Reformats a block of text (from cursor to the next blank
                line) and removes any hard CRs from the reformatted lines. It
                will add a hard CR to the end of the reformatted block.

        <C>     Line drawing    <Alt-F4>

                Allows you to draw lines and boxes using a variety of line
                sets.

                Undelete        <Alt-F1> or <Esc>

                Inserts the last deleted line at the current cursor position.
                The last eighty lines of deleted/marked text is always
                retained in a "scratch" buffer.

                Save & exit     <Alt-F10> or <Ctrl-Z>

                Save (or discard changes to) the current message.


                9.2.2 Toggle    <Ctrl-F2>

                Translation     <Ctrl-X>

                Toggles the state of the translation tables.

                Hard CRs        <Ctrl-C>

                Toggles whether or not hard CRs in the message text should be
                displayed.

                Echo info       <Ctrl-E>

                Toggles the state of the echo info. This function is only
                available in Conference folders.


            9.3 Utilities       <Alt-U>

            Survey              <Alt-F9>

            Invokes the message survey function.



                                          60




        <C> Force rescan        <n/a>

            Forces the Mailer and other Editors to rescan the NetMail folder.

            Move/copy           <Alt-J>

            Allows you to move or copy the current message to another folder.

            Message to file     <Alt-V>

            Exports the current message to an ASCII file. If the specified
            file already exists, you will be asked if you want to overwrite
            its contents or append the message to the end of the file.

            Print message       <Alt-I>

            Adds the current message to the print queue. Messages added to
            the queue are printed in the order they were added. If you
            attempt to leave the Editor while messages are still being
            printed, it will ask you to confirm your choice to exit. If you
            choose to exit, the Editor will cancel the remaining messages in
            the print queue.

            >>> The Editor does NOT use any external print spooler, such as
                DOS' PRINT program.

            Renumber            <Alt-B>

            Renumbers the messages in the current folder so that there are no
            gaps in the numbering. This function is not available in Hudson
            Message Base-type folders.

            Change username     <Alt-G>

            Allows you to change the current user profile.

            Change address      <Alt-W>

            Allows you to change the active network AKA (address). This will
            also change the address that is inserted in origin lines in
            Conference folders.

            Change origin       <Alt-O>

            Allows you to change the active origin line. Whether or not an
            origin line is appended to messages that you create is determined
            by the echo info setting (Conference folders only).

        <C> Drop marker         <Ctrl-D>

            Allows you to drop a marker (0-9) on the current message. You can
            later return to these markers by pressing <Alt> in combination
            with the digits 0 through 9.





                                          61




            9.4 Purge           <Alt-P>

            The options on the Purge menu allow you to remove one or more
            messages in the current folder, based on the various criteria, as
            described below.

            From user

            Purge all messages FROM the specified user.

            To user

            Purge all messages TO the specified user.

            From net address

            Purge all messages that originated from the specified address.

            To net address

            Purge all messages destined for the specified address.

            Received

            Purge all received (read) messages.

            Sent

            Purge all sent messages.

            Age

            Purge all messages older than the specified date.


            9.5 Help            <Alt-H>

            Keyboard help       <Ctrl-F1>

            Displays a brief help screen about various keys (cursor keys,
            etc).

            Macro keys          <Alt-K>

            Displays the contents of the 20 (24) macro keys available in edit
            mode.

            Program notice      <Ctrl-A>

            Displays the program version, copyright and registration
            information.

            Show notes          <Alt-X>

            Displays extended information about the currently displayed
            message. The extended information is stored behind Ctrl-A (ASCII
            1, SOH) characters in the message text.

                                          62




        <C> Remote Info         <Alt-Y>

            Displays information about the originating or destination system.


            9.6 Entering new messages

            Press <Ins>. The screen will be refreshed and you will be
            prompted for the destination. If you are in the NetMail folder,
            you can use the name/address look-up function to specify the
            destination of the message; if you are in a Conference or Local
            folder, you must type the destination manually.

            Once you have specified the destination of a message, you will be
            prompted for the subject (Re:). If you want to send or request
            files to/from another system, select the proper status bits and
            specify the file data in the subject line. Note that the default
            message status (specified in FDSETUP) is always added, but can be
            changed.

            Enter the message text and press <Ctrl-Z> or <Alt-F10> to save
            the message.


            9.7 Message survey  <Alt-F9>

            The Survey function is used to perform global operations on a
            range of messages such as moving, printing, copying, deleting,
            etc.

            When you press <Alt-F9> for the first time in a folder, the
            Editor will scan all the messages in the folder and build a list
            of them. That list is kept in memory until you press <Alt-F9> in
            another folder, or when the Editor, for some reason, has to
            rebuild its internal message list for the folder. If you remove,
            add or renumber messages the list will be updated accordingly, so
            no rescan is necessary.


                9.7.1 Main menu

                Kill            <Del>

                Removes all selected messages.

                Print messages  <F3>

                Prints all selected messages.

                Range select    <F4>

                Allows you to select a range of messages matching a certain
                criteria.

                Select all      <F5>

                Allows you to select all messages in the folder.

                                          63




                Move            <F6>

                Allows you to move all selected messages to another folder.

                Copy            <F7>

                Allows you to copy all selected messages to another folder.

                Export to file  <F8>

                Allows you to export all selected messages to an ASCII file.

                Go to message   <Enter>

                Returns to view mode and makes the highlighted message the
                current message.

                Select          <Space>
                Toggles the selected status of the highlighted message.

                Exit            <Esc>

                Returns you to view mode.


                9.7.2 Continuous tagging

                If you activate Caps Lock, messages can be tagged (selected)
                by moving the bar with the arrow keys.


                9.7.3 Range select  <F4>

                The range select function allows you to select a range of
                messages matching a certain criteria. Most of the functions
                only require a partial match with the selected search
                criteria.

                From user           <F2>

                Selects all messages from the specified user.

                To user             <F3>

                Selects all messages to the specified user.

                Originating address <F4>

                Selects all messages originating from the specified address.

                Destination address <F5>

                Selects all messages destined for the specified address.





                                          64




                Text                <F6>

                Selects all messages containing the specified search string
                in the message body.

                Date                <F7>

                Selects all messages between two dates.

                Re:                 <F8>

                Selects all messages matching the specified subject.

                Rcvd                <F9>

                Selects all messages with received (read) status.

                Sent                <F10>

                Selects all messages with sent status.

                Exit                <Esc>

                Returns you to the main menu of the Survey function.


            9.8 Keyboard macros

            The keyboard macros are located on <F1> - <F10> (12) and <Shift
            F1> - <Shift-F10> (12). When a macro key is pressed, the Editor
            will insert its contents at the current cursor position. The
            following macros are supported:

            Sequence        Expands to                        Key in FM
            ---------------------------------------------------------------
            ~~              ~
            ~|              |
            |               CR                                <Enter>
            ~B              TAB                               <Tab>
            ~>              Cursor one step to the right      <Right>
            ~<              Cursor one step to the left       <Left>
            ~^              Cursor one line up                <Up>
            ~V              Cursor one line down              <Down>
            ~G              Cursor to top of message          <Ctrl-PgUp>
            ~H              Cursor to end of message          <Ctrl-PgDn>
            ~F              Reformat paragraph                <Alt-F8>
            ~L              Insert line                       <Ctrl-Enter>
            ~Y              Delete line                       <Ctrl-Y>
            ~}              Delete from cursor to EOL         <Ctrl-End>
            ~T              Delete from cursor to EOF         <Ctrl-T>
            ~S              Save message and keep original    <Ctrl-Z>, 'N'
            ~#              Save message and delete original  <Ctrl-Z>, 'Y'
            ~U              Current username
            ~D              Recipient of original message
            ~O              Sender of original message
            ~A              Subject (re:) of original message
            ~C              Date of original message

                                          65




            ~J              Originating address of original msg
            ~K              Destination address of original msg

            ~!              Invoke DOS shell                  <Alt-Z>
            ~E<prog><parm>; Execute program
            ~X<filename>;   Export to file                    <Alt-V>
            ~I<filename>;   Import file                       <Alt-F2>
            ~R<filename>;   Import file and remove it

                Examples

                The sequence "~Edir /w>x.bak;~Rx.bak;" (without the quotes)
                will:

                    o   Execute "DIR /W>X.BAK"
                    o   Import X.BAK into the message text
                    o   Remove X.BAK

                Note that the semi-colon (;) is NOT optional for the
                "Execute" and "Import" macros. It determines the end of the
                program name and its parameters and/or the end of the name of
                the file to import.

                The sequence "|~T|~B~B~BRegards,|~B~B~B~U|" (without the
                quotes) will:

                    o   Insert a CR
                    o   Delete the text from the cursor to the end of the
                        message.
                    o   Insert another CR
                    o   Insert three TAB characters (equivalent to pressing
                        <Tab> three times).
                    o   Insert the text "Regards," without the quotes
                        followed by a CR.
                    o   Insert three TAB characters (equivalent to pressing
                        <Tab> three times).
                    o   Insert the current user's name followed by a CR.

                E.g.    ..
                        <message text>
                        ..

                                Regards,
                                John Doe


            9.9 Carbon copies (CC)

            The Carbon Copy function, is more or less what the name implies.
            A function that allows you to send the same message to two or
            more recipients; a distribution list. The CC function is only
            active in the NetMail folder. CCs can also be used for File
            Attach and File Request messages.





                                          66




            To use the CC function, put the text "cc:" (case does not matter)
            followed by one or more SysOp names or system addresses,
            separated by a comma, at the top of the message. Once you select
            to save the message, the Editor will scan the beginning of the
            message text for CC: and if found, process each element of the CC
            list. You can have more than one line with CCs.

                E.g.    cc: bremin,#bodger,samet
                        cc: howard,kasza,wallin,1:135/4

            Note that if you create several messages using the CC function,
            editing any of them will not reactivate the CC function. The
            Editor will only process a CC list the first time you enter a
            message (i.e. a new message).


                9.9.1 Hidden CCs

                To hide a recipient in a CC list, put the pound (#) character
                in front of the SysOp name or system address.

                    E.g.    cc: #1:135/20,#1:135/990,2:310/11


                9.9.2 Using files as input to CCs

                You can also specify a file containing SysOp names or
                addresses to the CC function.

                    E.g.    cc: @betanote.txt


                9.9.3 Address expansion

                All addresses in a CC list can be entered in short form, and
                several macros are recognized.

                    cc: MYNET

                Will process your whole net and add every system to the CC
                list. Note that the previously supported notation
                "MYNET/node" (eg. MYNET/12) is no longer supported.

                    cc: 2:310/*, 1:135/*

                Will include all systems in net 2:310 and 1:135.

                    cc: 2:270/17.*

                Will include all listed point systems under 2:270/17.


        <C> 9.10 Blind Carbon Copies (BCC)

            Blind Carbon Copies are identical to normal Carbon Copies with
            the exception that none of the recipients will know that the
            message is a Carbon Copy.

                                          67




        <C> 9.11 Crossposting (XC)

            Although CCs are not supported for Conference and Local folders,
            there is an additional function that provides you with a method
            of broadcasting the same message to two or more folders. This
            function is called Crossposting.

            To use the XC function, put the text "xc:" (case does not matter)
            followed by one or more numbers, separated by commas. Each number
            represents a folder number where you want the message
            cross-posted. If your folder list looks like:

                1   BNU
                2   COMP.SYS.IBM.PC
                3   FDECHO
                4   TSECHO
                5   NETSYSOP

            And you put "xc: 1,3,5" in a message in folder two. The resulting
            messages will have

                * Crossposted in BNU
                * Crossposted in COMP.SYS.IBM.PC
                * Crossposted in FDECHO
                * Crossposted in NETSYSOP

            At the top of each message. The target folder is excluded from
            the list. Ie. " * Crossposted in BNU " will appear in each
            message not going to the first (BNU) folder.


        10 Terminal

        Although FrontDoor was designed primarily as an e-mail system, it
        also features a powerful terminal emulator, hereafter called the
        Terminal. The Terminal features very accurate and efficient Terminal
        emulation and file transfer protocols; and several other features
        found in expensive and/or complex communications packages.

        The Terminal is invoked by pressing <Alt-J> from the Mailer's main
        menu, or by specifying /TERM on the command line when it is started.
        You can also choose to run the Mailer in terminal-only mode, in which
        case the Terminal is invoked up directly when you start it.

        Most functions of the Terminal are reached by holding down the <Alt>
        key and pressing a key, A through Z. If you press a key that has no
        function in the Terminal, it will display a message saying "Press
        Alt-H for help".










                                          68




            10.1 Menus

            Each function and menu of the Terminal will now be described.


                10.1.1 File         <Alt-F>

                The file menu contains functions to manipulate macros, upload
                and download files, transmit ASCII files, invoke DOS shell
                and Editor, etc.

                Download files      <Alt-G>

                Receive one or more files from the remote system.

                Upload files        <Alt-T>

                Transmit one or more files to the remote system.

                Transmit ASCII file <Alt-A>

                Allows you to transmit an ASCII file to the remote. You will
                be able to select the default inter-character delay and line
                translation. It is possible to create simple script or macro
                files by using this option.

                Macro management    <Alt-V>

                Allows you to create and maintain your macro key sets. Use
                this function to make a different macro key set the active
                set.

                Profile management  <Alt-E>

                Allows you to create, maintain, and select IEMSI session
                profiles. IEMSI is discussed in a separate section.

                Command history     <Alt-U>

                The Terminal records your last ten typed lines. When you
                press Enter, it removes the oldest entry and adds the newly
                typed line to the list. You can choose any one of the ten
                history entries and retransmit it to the remote.

                Editor              <Alt-I>

                Invokes the program defined in the Terminal > Miscellaneous >
                Editor field in FDSETUP. You will be asked for optional
                command line parameters, they are stored for the remains of
                your Terminal session. This could also be used to bring up
                external protocol menus, etc.

                Note that the FOSSIL driver is deactivated when leaving the
                Terminal and reactivated upon returning to the Terminal. This
                is to make sure FrontDoor maintain control of the FOSSIL
                driver even when loading other programs that could possibly
                leave the FOSSIL driver in a non-desirable state.

                                          69




                DOS shell           <Alt-Z>

                Invokes a temporary DOS shell. Type EXIT and press <Enter> to
                return to the Terminal.

                Leave Terminal      <Alt-Q>

                Depending on how the Terminal was invoked, this will return
                you to the Mailer's main menu or to DOS. If you are connected
                to a remote system when you press <Alt-Q>, you will be asked
                to confirm that you want to hang up.


                10.1.2 Line settings    <Alt-L>

                The line settings menu contains your current communications
                parameters. You cannot reach the options of this menu unless
                you press <Alt-L>. Most of the options in this menu are self
                explanatory, only the not so obvious options are explained
                here.

                BPS

                The current DTE baud rate. If you have enabled the "Lock
                port" option in FDSETUP, this field will contain "Fixed" and
                you will not be able to change it.

                Wraparound

                Determines whether or not the Terminal should place the
                cursor on a new line when it is positioned at the rightmost
                position of the screen and a character is received. This
                should be set to On in most situations. There are however
                VT100/VT52 applications that require this setting to be Off.
                Note that a CR/LF will force a new line even if this is set
                to Off.

                CR expansion

                Determines how a received CR character should be processed.
                If set to CR, no expansion is made. If, however, it is set to
                CR/LF, the Terminal will expand all received CR characters to
                CR/LF.

                Local echo

                Some on-line services do not echo the characters you type. It
                may be necessary to enable this option to see what you are
                typing. If the on-line service you are using does echo the
                characters you type and you enable this option, you will get
                duplicated characters. E.g. "HHEELLLLOO!!".







                                          70




                Emulation

                Allows you to choose between ANSI, VT100, VT52 and TTY (no)
                emulation. Note that the default for ANSI emulation is to
                support AVT/0+ (AVATAR/0+). This is a Terminal emulation
                protocol designed by G. Adam Stanislav. It is extremely fast
                and very efficient.

                Translation tables

                If enabled, the Terminal will use the Terminal translation
                tables to filter any received characters.

                Auto-Zmodem downloads

                The Terminal monitors received characters for the special
                sequence a Zmodem transmitter sends when a Zmodem file
                session is started. If it detects this start-up sequence, it
                will automatically invoke the Zmodem receiver. If you disable
                this option, you must use <Alt-G> (Download) to receive files
                using the Zmodem protocol.

                Allow AVT/0 sequences

                Determines whether or not you want to accept AVT/0+ emulation
                sequences when you are in ANSI emulation. Since AVT/0+ is
                based upon certain control characters, you may want to
                disable this option if you are using programs like Doorway,
                etc. which frequently transmits control characters.

                Clear on Form Feeds

                Determines whether or not the Terminal should clear the
                screen when receiving a Form Feed (FF, ASCII 12) character
                from the remote.

                Interactive EMSI

                Determines whether or not the Terminal should attempt to
                establish IEMSI sessions with systems you call. IEMSI is
                completely transparent and should not cause any problems.
                IEMSI is described in a separate section.


                10.1.3 Session      <Alt-S>

                Capture             <Alt-C>

                Allows you to capture characters, as they appear on the
                screen, to a disk file, or logging it to a printer. Since the
                Terminal filters out NUL characters (ASCII 0), they will
                never appear in a capture file.

                Other characters and control sequences may not appear either,
                depending on what terminal emulation protocol is active at
                the time.


                                          71




                Conversation mode   <Alt-N>

                The conversation mode function splits the screen in half,
                creating two windows or sections on the screen. Data received
                from the remote system will be displayed in the top section,
                while the characters you type will be displayed in the bottom
                section.

                Dial                <Alt-D>

                Allows you to dial a system in the nodelist. This function is
                disabled if no nodelist files are detected when the
                Terminal/Mailer is started. Note that you cannot queue
                numbers dialed via the nodelist.

                Manual dial         <Alt-M>

                Allows you to enter a number manually, which will then be
                dialed until you press the <Esc> key or a connection has been
                made. Note that you cannot queue manually entered numbers.

                Disconnect          <Alt-X>

                Disconnects the current call and displays the elapsed time.

                Phone directory     <Alt-P>

                Brings up the phone directory manager.

                Reset timer         <Alt-R>

                Resets the on-line timer. The timer is automatically reset
                when a new connection is made.

                Scroll back buffer  <Alt-B>

                Allows you to view data that has scrolled off the screen. The
                amount of data stored in the scroll back buffer is configured
                in FDSETUP.

                >>> If you invoke the Phone Directory and there is
                    insufficient memory available, the Terminal will dispose
                    of the memory allocated to the scroll back buffer in an
                    attempt to free sufficient memory to invoke the Phone
                    Directory.

                Send BREAK          <Alt-W>

                Sends a (short) BREAK signal to the modem. Consult the
                documentation for your modem regarding BREAK signals. This is
                often used to terminate inquiries to commercial on-line
                systems, etc. but can be treated differently by your modem.

                Clear screen        <Alt-J>

                Clears the screen and moves the cursor to the upper left-hand
                corner.

                                          72




        <C>     Initialize modem    <Alt-Y>

                Transmits the Init-1..Init-3 modem strings as configured in
                FDSETUP under Modem > Command strings, followed by the Init
                string defined under Terminal > Miscellaneous, to attempt to
                initialize the modem.


                10.1.4 Options      <Alt-O>

                Most Terminal emulators and communications packages have a
                status line, either at the top or at the bottom of the
                screen; on which they display various information about
                settings and the current connection. FrontDoor's Terminal
                does not have a status line, hence the options menu.


            10.2 Keyboard macros

            Depending on how many function keys you have on your keyboard,
            you will have access to 20 or 24 keyboard macros for every macro
            set. You can have over 60,000 macro sets defined, but only one
            can be active at any time. The macro management function is
            reached by pressing <Alt-V>.

            The keyboard macros are located on <Shift-F1> - <Shift-F10> (12)
            and <Ctrl-F1> - <Ctrl-F10> (12). When a macro key is pressed, the
            Terminal will send the data specified as the macro string,
            uninterpreted, to the remote system. The following characters
            have special meaning when specified in a macro string:

                Sequence        Expands to
                ----------------------------------------------------
                ~~              ~
                ~|              |
                |               CR
                ~B              TAB
                ~!              One second pause
                ~P              The current password as defined in the Phone
                                Directory or the current IEMSI Profile's
                                password.


            10.3 Raw mode

            The IBM PC keyboard generates two characters for every key you
            press. The first character is called the ASCII code, and the
            second character is called the scan code. Only the ASCII code is
            transmitted to the remote system by default. There are, however,
            some situations which require the Terminal software to transmit
            both codes. The AVATAR emulation protocol and the Doorway
            programs both require the complete codes (two characters) to
            identify certain keys; function and arrow keys in particular.

            >>> Once raw mode has been enabled (by pressing the Scroll Lock
                key), you cannot reach any of the Terminal's regular
                functions. Raw mode is disabled by deactivating Scroll Lock.

                                          73




            10.4 Keypad modes

            The VT100 and VT52 emulation protocols require that the cursor
            keys transmit different codes depending on the state of the
            remote application. Most on-line services follows the VT100
            recommendation for this, but several Editors and other programs
            have their own ideas of how this should be handled.

            If you enable the numerical keypad (Num Lock), the white cursor
            keypad will transmit the numerical application codes for
            VT100/VT52. If you have an extended (101/102) keyboard, the grey
            cursor keys will not follow the numerical keypad setting.

            By using the <Shift> key together with the white cursor keypad,
            you can negate the setting of Num Lock temporarily. Ie. if Num
            Lock is enabled and you press <Shift-Up> (8), the Terminal will
            transmit the up key sequence to the remote. If Num Lock is
            disabled and you press <Shift-Up> (8), the Terminal will transmit
            the numerical application keypad sequence for 8.


            10.5 PC keyboards

            When the remote (host) requests that the Terminal enters
            numerical application keypad mode, the Terminal automatically
            enables Num Lock. On extended (101/102) keyboards, this will also
            enable the Num Lock LED. The Num Lock LED on IBM-PC (standard)
            keyboards will not change by doing this. The Options, <Alt-O>,
            menu should correctly reflect the proper state of Num Lock
            anyway.


            10.6 Phone directory    <Alt-P>

            The phone directory allows you to define up to 200 (400 in the
            commercial version) numbers in addition to those stored in the
            nodelist database. The Terminal keeps the internal phone
            directory in a file named TERMPHON.FD, which is located in the
            SYSTEM directory.

            The top menu in the phone directory has nine options.

            Clear queue             <F1>

            Removes the queue (Q) status from all entries in the phone
            directory. If no entries are listed in the queue, no action is
            taken.

            Dial                    <F2> or <Enter>

            Adds the current (highlighted) number to the queue and proceeds
            to the dial function. If no connection is made, the Terminal will
            proceed to the next number in the queue. If no other numbers
            exists in the queue, the Terminal will wait the defined (in
            FDSETUP) number of seconds before trying again. You can abort
            dialing by pressing <Esc>.


                                          74




            Edit existing entry     <F4>

            Allows you to change an existing entry.

            Purge                   <F6>

            Removes all entries marked for deletion (small square) from the
            phone directory. There is no way to recover a removed entry, so
            use this option with caution.

            Toggle queue status     <F7> or <Space>

            Adds/removes the current (highlighted) number to the queue.

            Sort (and purge)        <F8>

            This option is similar to the Purge option with one difference.
            It will also sort the phone directory in ascending order, based
            on the name field.

            Add entry               <Ins>

            Allows you to add a new entry to the phone directory.

            Mark for deletion       <Del>

            Marks an entry for deletion (small square). No other action is
            taken. You must use the <F6> or <F8> function to remove entries
            marked for deletion.


                10.6.1 Queue status

                The queue status is only retained while you are in the phone
                directory. Once you return to the Terminal, the phone
                directory is removed from memory.


                10.6.2 Adding/changing entries

                When you press <F4> (Edit) or <Ins> (Add), the edit screen
                will appear. Press <F10> to save the entry and <Esc> to
                abandon the entry/changes.


            10.7 Inactivity timer

            If you are not connected to another system, the Terminal function
            will be terminated automatically after ten minutes of inactivity,
            if there is no carrier signal. The timer is reset if a key is
            pressed and when the carrier signal changes.







                                          75




            10.8 File transfers

            When you transmit or receive files in the Terminal, it will
            automatically set the line parameters to no parity, eight data
            bits and one stop bit. Once the transfer is completed, the line
            parameters will be reset to whatever values they had prior to the
            transfer.


            10.9 On-line timer

            The on-line time displayed in the Options, <Alt-O>, menu shows
            the elapsed time of the current connection in hours and minutes.
            It is not intended as a precise mechanism for cost calculations,
            etc. but will give you a rough estimate of the time you have
            spent on-line.


        11 Miscellaneous

        This chapter contains functions and options that are global to all
        programs in FrontDoor.


            11.1 Destination of messages

            When you are prompted for an address and/or SysOp name for a
            message, you can use the look-up function. This is true for both
            the Mailer, the Editor, and the Terminal. The Editor only allows
            you to use the look-up function for messages written in the
            NetMail folder.

            You do not have to use the look-up function, of course. You can
            enter a short form address, such as 10 (for node 10 in your own
            net), .1 (for point one in your own point net) in which case the
            SysOp's name is taken from the nodelist data. This is one of the
            most flexible functions in FrontDoor.


                11.1.1 Name lookups

                If you specify "Homrig" as the destination, you will be
                prompted to select from a list of all users with a last name
                matching "Homrig" (Homrighausen for example). The network
                address will also be taken from the name you select.


                11.1.2 Address browsing

                To enter the address browse mode, specify an incomplete
                address, such as "2:?", "2:270/?" or "2:270/17.?". You can
                then browse through all zones, regions, networks and
                pointlists known to your system.

                If you press <Enter> (and the input field is blank) when you
                are prompted for an address, you will be placed in browse
                mode in your own net.

                                          76




                11.1.3 Address macros (NAMES.FD)

                You can also create a file containing short names which
                expands into a full address/SysOp name. The macros are
                located in a file called NAMES.FD which must be placed in the
                SYSTEM directory. The format of NAMES.FD follows:

                        <alias>,<user name>,<address>[,<subject>]

                ALIAS       The name you want to use for the macro.

                USER NAME   The name you want FM to place in the TO: user
                            name field.

                ADDRESS     The network address you want as the destination
                            when using the macro.

                SUBJECT     The fourth and optional parameter can be used to
                            insert a default subject in FM and also in the
                            "File(s):" field in FD when using the "Mail
                            services" options "Request files" and "Transmit
                            files".

                    E.g.    oci,James Smith,1:132/300
                            am,AreaMgr,2:512/1,MyAreaMgrPassword
                            joho,joaquim homrighausen,2:270/17
                            jd,Jon Doe,9:333/111

                    Would allow you to place "*oci", "*am", "*joho", and
                    "*jd" anywhere you are prompted for a network address or
                    user name, including carbon copies (CC).

                A special format can also be used to automatically address
                messages to UUCP and INTERNET gateways. By putting a
                commercial at character (@) as the first character of the
                user name field (second field), you indicate to FM that the
                macro should receive special treatment.

                    E.g.    dn,@INTERNET/jd@jon.doe.lu,2:241/999

                            Would place "INTERNET" in the message header's
                            TO: field and address the message to 2:241/999.
                            On the first line of the message text, it would
                            put "TO: jd@jon.doe.lu".

                            If no forward slash (/) is found in the user name
                            field (where "INTERNET" is above), the Editor
                            defaults to putting "UUCP" in the message
                            header's TO: field.

                    This cannot be used for carbon copies (CC).







                                          77




        12 File Requests

        This section will explain and discuss the various aspects of File
        Requests. There are two types of Requests, File Request and Update
        Request. The latter is basically a File Request that triggers a
        mechanism to only send the requested files if they are more recent
        than those found on the requesting system. Two basic terms have to be
        explained and understood:

            Outbound Request

            A File or Update Request created and transmitted by your system
            to another, remote, system.

            Inbound Requests

            A File or Update Request transmitted by another system to your
            system.

        There is no mechanism in the Mailer to control how an outbound
        Request is treated by the remote system. The Mailer strictly deals
        with controlling the access to and security of your system (inbound
        Requests).


            12.1 Outbound Requests

            When you want to Request one or more files from a remote system,
            you may do so using several different methods:

                1.  By using the Editor and entering a message with File or
                    Update Request status. The files you want to request from
                    the remote system are listed on the subject (Re:) line of
                    the message and you set FilReq or UpdReq to indicate that
                    the Mailer should give the message special treatment.

                2.  By using the Mailer's temporary mail services, which are
                    accessed with <Alt-M> from the main menu. Whether or not
                    the Request is treated as an Update Request or File
                    Request is determined by how you specify the filename(s)
                    in the File(s): field. If you include a path, the Mailer
                    will treat it as an Update Request, otherwise, it will be
                    treated as a File Request.

                    Requests created this way will not remain if the Mailer
                    terminates (for one reason or another) as they are
                    intended for temporary, quick and dirty, purposes only.

                3.  Use a robot utility, such as XRobot, to create the File
                    or Update Request message(s).

            Note that an Update Request with no matching target, that is, you
            have attempted to Update Request a file that does not exist on
            your system, is automatically converted to a File Request.




                                          78




            12.2 Requesting files with a password

            Since files and directories can be protected with passwords, it
            may be necessary for you to present a password in order to
            request certain files from a remote system.

            To add a password to an outbound File or Update Request, you
            simply put the password preceded by a space character and a '!'
            character. Ie. <filename> !<password>. Regardless of whether you
            are creating the Request with the Editor or from the Mailer's
            Request function, this is the format used to specify passwords.


            12.3 Update Requests

            As mentioned before, an Update Request is really a File Request.
            The difference is that an Update Request is used to "update" a
            file that already exists on your system. The mailers accomplish
            this by transmitting the date and time of the existing file, the
            system that processes (receives) the Update Request then compares
            this with the requested filemask and sends any matching file that
            has a later date and time.


            12.4 Inbound Requests

            You can control which directories should be accessible from the
            "outside world" during a Request. This is accomplished by telling
            the Mailer which directories should be searched for matches. How
            the Mailer handles inbound Requests depends on how you have
            configured the Mailer > File requests section in FDSETUP.


                12.4.1 Request modes

                There are three different modes which decide how the Mailer
                treats a Request from a remote system. This is configured in
                the Mailer > File requests > Request limits section in
                FDSETUP.

                    1.  Anyone can request. This means that the Mailer will
                        allow any system to Request files from your system,
                        subject to event behaviors and other modifiers.

                    2.  Systems in nodelist can request. Similar to (1), but
                        the Mailer will only process Requests received from
                        systems that are listed in your nodelist database.

                    3.  No requests. Forces the Mailer to ignore any received
                        Requests, effectively disabling the ability to
                        request files from your system.







                                          79




                12.4.2 Directory listings

                The directories that the Mailer search during an inbound file
                request are configured in the Mailer > File requests >
                Filenames section of FDSETUP. Two files can be specified.
                Each file is a plain vanilla ASCII file with one directory
                (complete path) per line; this is NOT a filemask. All files
                in the specified directories will be available for file
                request. No other directories than those specified in these
                files will be searched.

                >>> The "List" file is searched during unsecure sessions
                    (i.e. those with systems that there is no session level
                    password for). The "SecList" file is searched during
                    secure sessions. This allows you to have different files
                    available depending on whether or not the session is
                    password protected. If no "SecList" file has been
                    specified, the Mailer will use the "List" file.


                12.4.3 Alias listings

                Alias files are used to set-up something often referred to as
                "Magic filenames". That is, the requesting system requests a
                specific name that expands into one or more files. The alias
                files are scanned before the list of requestable directories
                (see above), and if a match is made, the Mailer does not
                search the other lists. The two alias files are configured in
                the same section as the list of requestable directories.

                The alias file is a plain vanilla ASCII file with one alias
                definition per line.

                    E.g.    FRODO       C:\FILES\FRODO\FDKIT.ARJ
                            XR          C:\FILES\FRODO\XROBOT.ARJ
                            RA          C:\FILES\RA\RA*.ARJ
                            MYSECRET    C:\TEST1.ARJ C:\TEST2.ARJ

                The remote system can request FRODO, XR, RA, or MYSECRET and
                get the above specified files. Files listed as alias names do
                not have to be located in requestable (see above)
                directories.

                Just like you can specify different requestable directories
                depending on whether or not the session is password
                protected, you can specify two separate alias files.


                12.4.4 Response message

                In the event that the Mailer cannot satisfy a file or update
                request for one reason or another, it will return a message
                to the requesting system telling it why the request(s) could
                not be satisfied.




                                          80




                If you have specified a filename for the Message option,
                under Mailer > File requests > Filenames, the Mailer will
                attempt to open the specified file and append its contents to
                the end of the automatically generated response message.


                12.4.5 Limiting Requests

                You can choose to place a limit on how many files, how many
                kilobytes, and/or how long a request may take. This allows
                you to fine tune your system for maximum efficiency. The
                request limits are configured in the Mailer > File requests >
                Request limits section of FDSETUP.

        <C>     Stop after first match

                Prevents the Mailer from searching all requestable
                directories as soon as one match has been made for a given
                request.

                Maximum match (files)

                The maximum number of files your system will send during one
                Request session. If the remote system requests an alias
                filename that expands to two files, the request is counted as
                two files. A setting of zero disables this feature.

                Maximum time (minutes)

                The maximum time the resulting files of a request may take to
                transfer. Before sending each file, a check is made to see if
                sending the file will cause this limit to be exceeded. If so,
                the file is skipped and the next file in the list will be
                checked. A setting of zero disables this feature.

                Maximum size (KB)

                The maximum amount of data your system will send during a
                request session. Note that if the remote system requests an
                alias filename that expands into two files, the size of both
                files is checked. A setting of zero disables this feature.

                Minimum speed (BPS)

                The minimum baud rate required to allow Requests. If the
                current connection is at a lower speed, Requests will not be
                honored.


                12.4.6 Limited hours

                You may also choose to limit the access of your request
                functions to certain days and certain hours of those days.

                Limited

                Enables limited hours.

                                          81




                Start

                The time of day when your system should start honoring
                Requests. This setting can only be changed if the Limited
                hours option is enabled.

                End

                The time of day when your system should stop honoring
                Requests. This setting can only be changed if the Limited
                hours option is enabled.

                Days

                Defines on which days your system will honor requests.


                12.4.7 Event restrictions

                Ultimately, whether or not your system will honor requests is
                controlled by the current event's behavior. If the Allow file
                requests option for an event is set to NO, requests will not
                be honored.


                12.4.8 Protecting files and directories

                You may want to protect access to certain files and
                directories, just like another system may require you to
                present the proper password to request one or more files. See
                "Outbound Requests".

                The Request Manager in FDSETUP is used to protect Inbound
                Requests.

                    Filename/Directory

                    Defines the filename/directory you want to protect. This
                    is NOT an exclusive name. If you set this field to
                    C:\HIDDEN\ and define a password, all Requests that
                    result in files being sent from C:\HIDDEN\ are protected.
                    If you set this field to MYSECRET.ARJ and define a
                    password, the file MYSECRET.ARJ will only be sent if the
                    requesting system presented the proper password.

                    Password

                    Defines the password for the specified file/directory.
                    The requesting system have to present this in its request
                    to get the file(s). These passwords are treated case
                    insensitive.

                Entries with inactive status in the Request Manager are
                ignored by the Mailer. Note that Alias definitions can also
                be protected by placing the name of the Alias definition in
                the Filename/Directory field.


                                          82




        <+>     12.4.9 Request processor

                A request processor is basically a slide-in replacement for
                the Mailer's internal code to handle file requests. The main
                difference is that it is an external program and can thus be
                easily replaced and updated. Other advantages include being
                able to access proprietary file database formats used by some
                BBS packages, and to handle searches for files located on CD-
                ROM drives which are notoriously slow if you access them
                directly.

                The Request processor is configured in the Mailer > File
                requests > Request processor section of FDSETUP. The Name
                field is the program to invoke (i.e. the name of the request
                processor) and any parameters it may require. Several macros
                can be specified to give the request processor access to some
                of the Mailer's internal variables and data. The Enabled
                field simply determines if the Mailer should call the request
                processor or if it should handle file requests internally.
                The Swapping option determines if the Mailer should swap its
                program image out of memory prior to invoking the request
                processor.

                The available macros are described in the FrontDoor
                Developer's Kit (FDDEV) and the specific macros you have to
                use with the request processor should be covered by its
                documentation. There are at least two request processors
                available for FrontDoor at the time of publication; one works
                with the Maximus BBS software and the other with
                RemoteAcccess 2.x.


        13 Swapping

        Both the Editor and the Mailer require over 220 KB of RAM. If you
        shell to DOS, or load another program from the Mailer, this memory is
        not available for other programs. You can therefore force the Editor
        and the Mailer to swap their program image to disk or EMS/XMS memory.
        If you have specified that you want the programs to use XMS/EMS
        memory for swapping but there is not sufficient XMS/EMS memory
        available, the swap image is written to disk. The swap file is placed
        in the SYSTEM directory and removed when you return to the program.

        If you enable swapping for the Mailer, it will be swapped out when
        you invoke a DOS shell and when you invoke other programs. The Mailer
        swap setting also affects the Terminal. The Terminal will not flush
        its scroll-back buffer to disk if any type of swapping is enabled for
        the Mailer.

        Once the swap image has been created and written to XMS/EMS memory or
        a disk file, all memory used by the program is freed except between
        three and five KB which will always remain in memory.






                                          83




            13.1 Complete path specifications

            To avoid problems when you enable swapping, it is recommended
            that all the filename and directory specifications under Global >
            Filenames in FDSETUP contain complete path specifications,
            including a driver specifier.

            If you choose to swap to a disk file, it is further recommended
            that you specify a complete path to where you want the swap files
            to be placed (Global > FileNames > Swapping).


            13.2 Loading programs in a DOS shell

            Make sure that you do not load any TSR (Terminate and Stay
            Resident) programs, such as DOS' PRINT and SideKick, when you are
            in a DOS shell. Failure to follow this advice may lead to system
            lockups when you attempt to return from the DOS shell.


        14 CRT environments

        All programs in the FrontDoor package are screen environment aware
        and most of them can adjust to most (if not all) screen sizes as long
        as the current screen mode has 80 or more columns (horizontally).

        If you have an EGA or VGA card that allows you to set the screen mode
        to something like 132x28 and you want to use this in the Editor, the
        Mailer, or the Terminal, you should specify that you want the AUTO
        screen mode for that particular program. This will prevent it from
        altering the screen mode.

        Please note that if you run the Mailer in AUTO mode, you must run the
        Editor and the Terminal in AUTO mode as well, if you plan to invoke
        either from the Mailer (and not just from DOS). Otherwise, the Mailer
        will display garbage on the screen when you return from the Terminal.
        The opposite (running the Terminal in AUTO and the Mailer in 25 or
        43/50) is, however, properly handled.

        <+> The registered version also allows you to use an alternate mode
        referred to as Custom, which allows you to specify the exact register
        parameters to the INT 10H Video BIOS call. Refer to the documentation
        for your video adapter for further information.


        15 Message Status Bits

        Message status bits determines how the Mailer will treat outbound
        (outgoing) messages and how the Editor will treat locally destined
        messages. The Message status menu is accessed by pressing <Alt-S> in
        the Editor and is also displayed when entering a new message and
        changing the subject of a message.






                                          84




        The keys listed refer to the status menu in FM.

        Private         <Ctrl-P>

        Indicates that the message should only be read by the addressee.

        Crash           <Ctrl-C>

        High-priority mail. Messages with crash status can never be routed or
        held by a route file (see Mail routing). Crash messages do, however,
        NOT override any cost restrictions for an event; they also require
        that the destination system has been qualified before the Mailer will
        call it.

        Hold            <Ctrl-H>

        The hold status will force the Mailer to ignore the message unless
        the destination system calls your system to pick up its mail. If the
        message is destined for a point system and the boss of the point
        system calls your system, the message will be given to the boss
        unless the message also has Direct status.

        File            <Ctrl-F>

        Indicates that the message has one or more files attached to it. The
        files are listed in the subject (Re:) line. File attach messages can
        be routed and held unless another status bit (Crash, Immediate, Hold,
        etc.) prevents it. The default treatment of a file attach message is
        to send it directly to its destination.

        File request    <Ctrl-R>

        Indicates that the message is a File Request. The requested files are
        listed in the subject line and may contain wild-cards characters.
        File request messages can be held, but are never routed. See "File
        Requests".

        Update request  <Ctrl-U>

        Similar to a File Request, but the subject line (Re:) must contain
        valid (existing) file specification(s). When the Mailer connects to
        the destination system, the requested files will only be sent by the
        remote if they are more recent than the matching files on your
        system. See "File Requests".

        Kill/sent       <Ctrl-K>

        Removes the message after it has been sent or picked up. If the
        Kill/Sent status is not set on a message, it will be marked as sent
        after it has been sent or picked up.

        Trunc/sent      <Ctrl-T>

        Truncates the attached files to zero length after they have been sent
        or picked up. This option is only valid for file attach messages.



                                          85




        >>> Note that it is nearly impossible to recover a truncated file so
            use this option with caution.

        Delete/sent     <Ctrl-E>

        Removes the attached files after they have been sent or picked up.
        This option is only valid for file attach messages.

        Direct          <Ctrl-D>

        Similar to the Crash status, with the difference that they can be
        held. Messages with the Direct and Hold status combined require that
        the destination system (including points) call in to pickup their
        mail.

        Immediate mail  <Ctrl-I>

        Similar to the Crash status, but messages with immediate status will
        be sent at the first opportunity, ignoring all restrictions and
        qualifications. If there is one or more messages with immediate
        status to a system, all other messages (except those with hold
        status) to that system will be added to the mail packet. USE THIS
        OPTION WITH CAUTION!

        Lock            <Ctrl-L>

        Locks a message from further access. This is done by setting the DOS
        attribute to read-only and adding a special flag to the message text.
        The Mailer and most other utilities will ignore message files (.MSG)
        with read-only attribute.

        Messages with lock status cannot be removed by any of the purge
        functions and will never be sent (or picked up). The Editor can,
        however, renumber a folder containing one or more messages with
        locked status.

        Sent            <Ctrl-S>

        Indicates that the message has been sent or picked up by the
        addressee. Once a message has been flagged as sent, they cannot be
        sent or picked up by the addressee.

        No status       <Ctrl-Z>

        Clears all status bits. This is actually a toggle. I.e. if you press
        <Ctrl-Z> once, the Editor will remove all status bits (except the
        Local bit), if you press <Ctrl-Z> again, the Editor will restore the
        previous status bits.


        16 Mail routing

        This is one of the most complex parts of FrontDoor and takes
        considerable time to learn and understand. Make sure you understand
        how each routing verb affects mail routing before you use it.



                                          86




        When the Mailer is brought up, it scans for any active events and
        when one is found, opens the route file, ROUTE.FD, and uses it to
        determine whom to send mail to, and how to send it. The route file
        must be placed in the SYSTEM directory. If the timestamp of the route
        file is modified, the Mailer will detect it and rescan the NetMail
        folder (see "Semaphores").

        Global routing commands are those that appear before any SCHEDULE
        keyword in the route file. They are always used, so you can specify
        routing that is identical for all your events here.

        Local routing commands are those that appear between two SCHEDULE
        keywords (a "Schedule block") in the route file. the Mailer
        determines which schedule block to use by searching for a schedule
        keyword with a tag (letter) matching the current event tag (see
        "Events").

        Several references are made to Hold status in this chapter. Do not
        confuse this with the HOLD command. The Hold status refers to the
        message status bit (see "Message Status Bits"), or where stated, to a
        system's nodelist status.

        The Mailer allows you to insert comments in your route file. Every
        line with a semicolon as the first non-space (TAB/Space) character is
        treated as a comment. While comments may seem inadequate at first
        glance, it is a very useful function. Going back to a route file you
        wrote five months ago may not be your definition of spending a
        weekend in joy and happiness.

        Addresses specified in the route file should always be fully
        expressed. The * macro (implying "ALL") is supported. You can also
        use any combination of nodelist flags to specify a range of systems.
        The routing language is case insensitive (case does not matter).
        SCRIPT, SCripT, and scRIPt are all treated as the same command.


            16.1 Default routing

            The Mailer has several default rules for routing that will be
            used if no other rules have been defined for a specific system.
            Some of the default rules cannot be overridden by routing
            commands.


            16.2 Message status

            Messages with immediate (IMM hereafter), Crash, File/Update
            Request, and Direct status will normally not be routed. They are
            sent directly to the destination system, with the exception of
            systems without a telephone number, as described later.

            Messages with IMM or Crash status can never be held by using the
            HOLD command. Messages with Crash status can, however, be
            prevented from being sent by event behavior, qualification lists,
            and cost restrictions.



                                          87




            Messages with Hold status will NEVER be packed into a mail
            packet. They can always be picked up by the destination system
            (unless they also have Lock status). Messages to points with Hold
            status can and will be picked up if the Boss of the point calls
            to pickup mail, unless the message also has Direct status.

            Messages with IMM status will always be packed into mail packets,
            overriding event restrictions. If you have a message with IMM
            status, the Mailer will add all other qualifying messages to the
            same system to the same mail packet.

            Messages with Rcvd (read), Orphan, Lock, and/or Sent status are
            ignored by the Mailer.


            16.3 Host/Hub/Boss routing

            Messages not otherwise prevented from being routed will by
            default be sent to the destination system's Host (see "Nodelist")
            if the destination system is outside your own net and to its Hub
            if it is within your own net.

            If you have mail for a system listed as DOWN in your nodelist
            database, it will never be packed. If the system calls your
            system to pick up mail, it will receive its mail.

            If you have mail for a system listed as HOLD or PVT (no telephone
            number) in your nodelist, the default behavior is to send the
            mail via the system's Host, Hub, or Boss. If the mail to a HOLD
            or PVT listed system contains file attaches, the mail packet will
            by default be placed on hold for the Host/Hub, or go directly to
            the Boss in the case of a point.

            Messages to systems not in your nodelist (unlisted systems) will
            not be Host/Hub routed by default, but they can be explicitly
            routed.

            Messages with Crash, IMM, or Direct status, destined for points
            to which the Mailer cannot place a call directly will retain its
            status (and restrictions), but the Mailer will instead assume the
            point system's Boss as the destination.


            16.4 Qualifying systems

            Before the Mailer will send mail to a system, it must be
            qualified by specifying its address, or a macro that includes its
            address in a SCHEDULE block (this is not true for IMM mail as
            previously described).

            You can qualify a system by placing a SEND-TO command in the
            global section of a route file, but this is NOT RECOMMENDED.
            SEND-TO, POLL and the optional SEND-LIST after a SCHEDULE command
            are the only available methods to qualify a system for mailing.




                                          88




            If the Mailer cannot find ROUTE.FD, mail to all systems will be
            put on hold for the destination system to call in and pickup its
            mail.


            16.5 Route commands

            SCHEDULE <TAG> [SEND-LIST]

            Defines the start of a schedule block. All commands following a
            SCHEDULE command are considered a part of the same block until
            another SCHEDULE command is encountered.

            TAG is a letter corresponding with the event tag, defined in
            FDSETUP (see "Events"). You should only have one schedule block
            per defined event tag.

            The optional SEND-LIST parameter should contain the systems to
            qualify for the event.

            SEND-TO <SEND-LIST>

            Qualifies the specified systems. This is identical to the
            optional SEND-LIST after the SCHEDULE command.

            HOLD <LIST>

            Hold mail for the specified systems.

            UNHOLD <LIST>

            The opposite of HOLD. Useful if you have used the HOLD command in
            the global section and want to negate the effect of those for one
            or more systems.

            NO-ROUTE <LIST>

            Send mail to the specified systems directly. This overrides the
            default routing rules. Some logics is applied to "directly" when
            using the NO-ROUTE command. Systems which the Mailer cannot mail
            directly will be sent "as directly as possible".

            E.g. if <LIST> includes a system listed as PVT (no telephone
            number), the Mailer evaluates the "NO-ROUTE" as "NO-ROUTE this
            message to the system's nearest Host/Hub".

            DIRECT <LIST>

            Unconditionally send mail to the specified systems directly (you
            can still place it on hold by using the HOLD command). No implied
            logics is applied to this command, and if the Mailer cannot call
            the specified systems, the resulting mail packets are placed on
            hold automatically. Note that a system must still exist for this
            to apply. If a system that is included in a DIRECT <LIST> does
            not exist, the message will be stamped "Orphan" and not included
            in a mail packet, but it can still be picked up by the
            destination system.

                                          89




            ROUTE-TO <TARGET> <LIST>

            Route mail (excluding file attach messages) for the specified
            systems via TARGET. This automatically implies "NO-ROUTE
            <TARGET>", i.e. the target system's mail will not be routed
            through another system, even if so previously stated.

            HOST-ROUTE <LIST>

            Route messages, not otherwise prevented from being routed, for
            the specified systems through their Host system.

            HUB-ROUTE <LIST>

            Route messages, not otherwise prevented from being routed, for
            the specified systems through their Hub system.

            ROUTE-FILES <TARGET> <LIST>

            Route file attach messages (and normal mail) for the specified
            systems through TARGET. This automatically implies "NO-ROUTE
            <TARGET>", i.e. the target system's mail will not be routed
            through another system, even if so previously stated.

            You should ask the SysOp of the TARGET system if he allows you to
            route files through his system before using this command.

            POLL <LIST>

            Force the Mailer to call the specified systems even if there is
            no other mail destined for them. This does not effect the routing
            of existing mail destined for the specified systems. The POLL
            command unconditionally qualifies a system for mailing. Each
            system in LIST will only be called once. If an event is
            restarted, the Mailer will not call systems that it has already
            polled.

            EXCEPT <LIST>

            Specifies an exception to the LIST of the previously used
            command.

            FORWARD-FOR <LIST>

            Tells the Mailer that you allow the specified systems to send
            mail (excluding file attach messages) through your system. Note
            that this does not place any restrictions of the destination of
            the forwarded mail.

            FORWARD-TO <LIST>

            Tells the Mailer that you allow mail (excluding file attach
            messages) to be forwarded through your system ONLY if it is
            destined to any of the specified systems. This is a more secure
            alternative to the FORWARD-FOR command.



                                          90




            FILES-FOR <LIST>

            Identical to FORWARD-FOR, but for file attach messages.

            FILES-TO <LIST>

            Identical to FORWARD-TO, but for file attach messages.

            DENY <LIST>

            Allows you to prevent the specified systems from picking up
            waiting mail. The Mailer will still accept incoming mail from the
            specified systems. This can be used to prevent local (or other
            low-cost) systems from picking up their mail in national mail
            events, etc.

            SCRIPT <SCRIPT FILE> <LIST>

            Tells the Mailer to use the SCRIPT FILE when calling the
            specified systems instead of the telephone number (if any) in
            your nodelist database. Script files are explained in a separate
            section.

            NO-SCRIPT <LIST>

            Prevents the Mailer from using default script handling for the
            specified systems. Script files are explained in a separate
            section.


            16.6 LIST specifications

            You can use a variety of formats to specify a list of systems for
            a routing command. A few follows:

                *           All systems

                2:*         All systems in zone two

                2:270/*     All systems in zone two, net 270.

                2:270/1     2:270/1 and all points under it.

                2:270/1.0   2:270/1 but no points under it.

                2:270/1.1   2:270/1.1.

                MYNET       All systems in your own net. Note that the result
                            of this format depends on which AKA FD is
                            operating under. This is normally your primary
                            AKA.







                                          91




            16.7 Using nodelist flags

            When you specify system LISTs to a routing command, you can use
            nodelist flags in place of address information. Any combination
            of nodelist flags can be used. You can mix flags and address
            information as you wish. A few follows:

                %HST %CM        All systems with HST or CM in their nodelist
                                entry.

                %!HST           All systems that do not have HST in their
                                nodelist entry. The ! character negates the
                                meaning of a flag.

                %!HST %!CM      All systems that do not have HST _or_ CM in
                                their nodelist entry.

                %!HST %CSP      All systems that do not have HST in their
                                nodelist entry and all systems that have CSP
                                in their nodelist entry.

                1:1/5 %HST %CM  1:1/5 and all other systems with HST or CM in
                                their nodelist entry.


            16.8 File routing/forwarding

            FILES-FOR and FILES-TO will mark all in-transit (not destined for
            your system) file attach messages as Del/Sent (see "Message
            Status Bits"). If you receive the same file destined for two
            different systems, the file will not be removed until it has been
            sent to (or picked up by) both systems.


            16.9 Message forwarding

            When the Mailer unpacks received mail packets, it will always
            mark messages as in-transit if they are not destined for your
            system (including any AKAs). These messages can be forwarded by
            using FORWARD-FOR and FORWARD-TO, but the Mailer will under NO
            circumstances forward mail, that has not been entered or modified
            locally, automatically to systems unless one or both of these two
            commands are used.


            16.10 Multiple zones

            If you are operating under more than one AKA listed in different
            zones, it is important to explicitly specify a zone for address
            information in the route file.








                                          92




            16.11 Examples

            Here are a few examples of route files and how to use route
            commands:

                schedule @ *

            This is the most simple of route files and qualifies all systems
            for mailing. It will force the Mailer to use its default routing
            rules for mail to all systems.

                schedule @ *
                    route-to    2:512/1 2:*
                    hold        2:512/1 %!CM %!HST

            This qualifies all systems for mailing, routes all mail destined
            for zone two through 2:512/1, and places the mail for 2:512/1
            (including the routed mail) and any systems, that do not have the
            CM or HST flags in their nodelist entry, on hold.

                schedule @ MYNET

            This qualifies all systems in your own net and uses default
            routing.

                schedule @
                    send-to     1:* 2:* 3:*
                    route-to    2:512/1 2:*
                        except  2:201/329
                                2:201/130
                    route-to    3:632/348 3:*
                    deny        MYNET

            This qualifies all systems in zone one, two, and three. Routes
            all mail destined for zone two through 2:512/1 except for mail
            destined 2:201/329 and 2:201/130, routes all mail destined for
            zone three through 3:632/348, and prevents systems in your own
            net from picking up their mail.

                schedule B *
                    hold        *
                        except  2:*
                    no-route    2:*

            This qualifies all systems, holds all mail except mail destined
            for systems in zone two, and sends mail destined for zone two
            directly to its destination.

                hold *

                schedule D MYNET
                    unhold MYNET

                schedule A 1:*
                    unhold 1:*



                                          93




            This holds all mail by default (the HOLD command is in the global
            section).

            Schedule D sends mail to all systems in your own net.

            Schedule A sends mail to all systems in zone one.


            16.12 Dynamic packing

            Whenever a mail event is started, the Mailer scans the messages
            in the NetMail folder and possible packets are built. Messages
            that do not qualify to be processed will not be packed (but kept
            in the internal list). If a system calls in, the Mailer will scan
            the list stored in memory and create a mail packet "on the fly"
            and immediately send it to the calling system. So mail is always
            available, 24 hours/day.

            This means that your system does not have to be in a specific
            event for other systems to pickup their mail. Note that you can
            prevent systems from picking up their mail with the DENY command
            and by modifying an event's behavior.


            16.13 Regarding points

            Points of other systems are always treated as their boss system
            unless you explicitly specify the boss or a point. To ONLY
            reference a boss system, without referencing its points, use .0
            (eg. 2:270/17.0).

            If you have the telephone number for another system's points, the
            will be treated just like any other node. Ie. you can send mail
            to them directly.


            16.14 Order of evaluation

            The route file is evaluated (processed) from top to bottom.
            Because of this, it is wise to put the "global" (affecting all
            systems) first, followed by the exceptions. E.g.

                route-to    2:512/1 *
                no-route    2:270/17

            will result in all mail being routed via 2:512/1, except mail for
            2:270/17, which is sent directly to 2:270/17.

            The only route command that cannot be overridden in this manner
            is the ROUTE-FILES command. It is therefore required that you use
            the EXCEPT keyword to override a ROUTE-FILES command where
            necessary. E.g.

                route-files 2:512/1 *
                    except  2:270/17



                                          94




            will result in all file attaches messages being sent via 2:512/1,
            except file attach messages destined for 2:207/17, which are sent
            directly to 2:270/17. The only other way to override the effects
            of a ROUTE-FILES command is to use the DIRECT command.


            16.15 TARGET vs. qualification

            Note that only actual <TARGET> systems, and systems which you
            have told the Mailer to send mail directly to, or systems not
            otherwise included in default routing, need to be qualified.

                route-to    2:512/1 *
                no-route    2:270/17

                schedule @ 2:512/1 2:270/17

            Note that even if you have mail for a non-qualified system (i.e.
            a system other than 2:512/1 and 2:270/17), it would be routed to
            2:512/1, and qualified for sending (via 2:512/1), using the above
            scenario.


            16.16 Restrictions

            A <TARGET> system cannot contain a point address.

            You can not route mail destined for your own systems via another
            system.


            16.17 Macros

            MYZONE      All systems in your zone.
            MYNET       All systems in your net.
            MYPOINTS    All points under your system.


            16.18 Supported nodelist flags

            All past, present, and future nodelist flags are supported. There
            is, however, one case that is not dealt with automatically. The
            FidoNet nodelist contains several "user flags" of which only the
            first flag is preceded by a single 'U', e.g. UISDN,REC and
            UREC,ISDN. To specify such a flag in the route file requires that
            you specify the actual string since the Mailer requires an exact
            match. E.g. "%ISDN" would NOT match "UISDN". To be on the safe
            side, it is recommended that you specify user flags with and
            without the preceding 'U' - "%ISDN %UISDN". Note that the meaning
            of flags can be negated by placing a '!' character in front of
            them, eg. %!HST.

            >>> All FrontDoor systems should have the "XA" flag in their
                nodelist entry.




                                          95




        17 EMSI and IEMSI

        EMSI (EMSC-001 and FSC-0056) or "Electronic Mail Standard
        Identification" is a handshake method developed by Joaquim
        Homrighausen and Chris Irwin (author of D'Bridge). It provides
        features and flexibility that other handshake methods, such as FTS-1
        and FTS-6 (YooHoo), do not offer.

        The two major advantages of the EMSI handshake method is the ability
        to pickup mail for all your AKAs in one call, and unlimited expansion
        of the data (handshake packets) exchanged when a session is
        negotiated. I will not go into any technical details about EMSI here,
        I will, however, describe the handling of the multiple AKAs.

        The EMSI handshake is supported by FrontDoor, FrontDoor APX,
        TrapDoor, BinkleyTerm, and D'Bridge. EMSI does not interfere with
        other handshake protocols such as FTS-1 and FTS-6.


            17.1 Passwords

            If you have established or wish to establish a session level
            password for a certain system, you must make sure that you have
            entered all AKAs of that system in the Security Manager. All
            entries must have the same password.

            For example, let us assume you want to establish a session level
            password with 1:135/142 which is also 26:1305/142. You should add
            both 1:135/142 and 26:1305/142 in the security manager and use
            the same password for both entries.


            17.2 Mail

            Using the same example, if you have mail for both 1:135/142 and
            26:1305/142, all mail (for both addresses) would be delivered
            during the same session. This is true for both inbound and
            outbound connections.

            If you know that a system is EMSI capable and you have regular
            mail traffic with more than one of its AKAs, you can HOLD mail
            for the system's other AKAs and only allow the Mailer (FD) to
            call one of the addresses. When the session is established, all
            of the remote system's AKAs are processed.

            This probably sounds more confusing than it really is. So to make
            a long story short, make sure you have the "Present all AKAs to
            remote" option enabled (Mailer>Miscellaneous) and play it by ear.


            17.3 IEMSI

            IEMSI is similar to the EMSI handshake protocol, with the
            exception that it deals with the handshake between a terminal
            program (such as the one found in FrontDoor) and an on-line
            service, such as a BBS.


                                          96




        18 Script language

        The script language provides an alternative method of calling a
        system (instead of calling it directly with the telephone number
        listed in your nodelist). A script file is used where you have to, or
        prefer to, connect to another system indirectly. I.e. you will not be
        calling it by dialing its number directly. This could be through X.25
        or PC Pursuit to name a few.

        The script file must be a plain vanilla ASCII file. A semicolon (;)
        may be used as a comment character, forcing the Mailer to ignore
        everything following the semicolon on the same line. The Mailer is
        not case sensitive when interpreting the script file.

        The route file (ROUTE.FD) can be used to specify that a script should
        be used for one or more nodes by entering:

            SCRIPT <SCRIPT FILE> <LIST>

        (see Mail routing). The command may be global or local to a specific
        event's schedule block. If you are using PC Pursuit, you can use a
        generic script file for all "PC Pursuitable" nodes. See PCP SCRIPTS.


            18.1 What can I do with it?

            The script language consists of a number of commands that allows
            you to send characters to the modem, wait for responses from the
            modem or the remote system/network that you are using, and
            trigger different actions depending on the responses you get.

            The versatility of the script language is further enhanced by the
            use of so-called labels to execute different parts of the script
            depending on a specific situation. The script language can be
            seen as a simple programming language for controlling the way FD
            or the Terminal makes a call.


            18.2 Commands

            SEND <STRING>

            Sends a series of characters to the modem or the remote system.
            Everything following the SEND command on the same line will be
            sent. Control characters may be entered using mnemonics, e.g.
            <CR>. In addition, <CR> (carriage return) may be sent by using
            the pipe (|) symbol. The string will be sent exactly as entered,
            with no case conversion.

            DIAL <NUMBER>

            Sends NUMBER, preceded by the dial command specified in FDSETUP's
            modem section. Control characters may be entered in the same
            manner as with the SEND command.




                                          97




            SETPORT <BAUD> <DATABITS> <STOPBITS> <PARITY>

            Sets the communications port to the specified parameters. BAUD
            can be any value supported by the hardware between 300 and 9600
            baud. At no time will the baudrate be set to a higher value than
            the highest supported speed of the destination system, or the
            baudrate of the outbound node in a PC Pursuit script. DATABITS is
            7 or 8. STOPBITS is 1 or 2. PARITY is NONE, ODD or EVEN. In
            addition, a value of -1 means that the previous setting for that
            parameter should be retained.

            PROVOKE <STRING>

            Keeps sending STRING with an interval of one second, until any
            character is received from the remote system, or until a timeout
            occurs (see TIMERSET), or until the script interrupted by the
            user. Control characters may be entered in the same manner as
            with the SEND command.

            TIMERSET <SECONDS>

            Sets the timer for fatal timeouts while waiting to receive
            something from the remote system. The default is 120 seconds (two
            minutes). The maximum value is 300 seconds (five minutes), and
            the minimum is 0.

            DEBUG <ON|OFF>

            Sets debug mode on or off. In debug mode, all characters received
            while waiting for one or more strings will be displayed. When you
            are not using debug mode, only the string that matched a pattern
            will be displayed. Similarly, in debug mode all strings sent to
            the modem/remote system will be displayed, whereas the Mailer
            will only display "Sending string" when not using debug mode. It
            is recommended that you enable debug mode while developing and
            testing a script.

            WAIT <SECONDS>

            Makes the script wait for SECONDS seconds before continuing.

            WAITFOR <STRING>[|<STRING>|<STRING>..]

            Forces the script to wait for one or more specified strings or
            until a timeout occurs (see TIMERSET). Each string must be
            separated with a pipe (|) character. Control characters may be
            entered in the same manner as with the SEND command. Of the
            specified strings, only the first will signify success, the other
            strings will immediately terminate the script with failed status.
            The string comparison is case sensitive, and requires an exact
            match.







                                          98




            CASE / ENDCASE

            Starts and ends a CASE statement, respectively. CASE is a more
            flexible variety of WAITFOR. Each line after CASE must start with
            a string that the script should wait for, followed by a colon and
            one or more script commands, or a label jump directive (see
            LABELS).

            If the string consists of more than one word, it must specified
            between quote characters ("). The CASE statement is ended with
            the command ENDCASE on a separate line.

            When a matching string has been received from the modem or the
            remote system, the command on the same line will be executed. If
            the command consists of a label jump instruction, the script will
            continue from the specified label position. If it is one or more
            script commands, they will be executed, and the script will
            continue from the line following the ENDCASE statement, unless
            the command terminates the script (see SESSION and FAIL).

            The string comparison is case sensitive, and requires an exact
            match. A short example follows.

                    CASE                            ; Comments:
                        CONNECT     :   session     ; connect
                        BUSY        :   >redial
                        "NO CARRIER":   >redial
                        VOICE       :   fail
                        @NOCARRIER  :   fail        ; carrier lost
                        @DEFAULT    :   fail        ; timeout
                    ENDCASE


            @NOCARRIER

            Tests the presence of carrier in a CASE statement.

            @DEFAULT

            May be used to specify a default course of action if a timeout
            occurs in a CASE statement.

            SESSION

            Terminates the script with success status, leading to a mail
            session if the script was invoked from the Mailer. It is NOT
            necessary to have a SESSION command in script files used to
            connect to another system in the Terminal. The SESSION command is
            only used to establish mail sessions.

            FAIL

            Terminates the script with failed status. No mail session will be
            initiated.




                                          99




            PURGEIN

            Purges the inbound buffer, getting rid of any pending characters.

            PURGEOUT

            Purges the outbound buffer, getting rid of any pending
            characters.

            RETRYCOUNT <RETRIES>

            Provides a means of incrementing and checking a predefined retry
            count variable. If the retry count exceeds RETRIES, the script is
            terminated with failed status, otherwise the count is incremented
            with 1. The retry count does not include the first attempt.

            CLEARCOUNT

            Clears the predefined retry count variable, resetting it to 0.

            MAX2400 <COMMANDS>
            MAX1200 <COMMANDS>

            Commands following on the same line will only be executed if the
            max baudrate for the session is 1200/2400. The maximum baudrate
            for a session is calculated as the maximum baudrate supported by
            the remote system, by the outbound node (if using PCP), or by
            your own modem, whichever is lowest.

                Eg. MAX2400 setport 2400 -1 -1 -1
                    MAX1200 setport 1200 -1 -1 -1

            @OUTBOUND

            Used to insert the name of an outbound PC Pursuit node in a
            string. The contents of @OUTBOUND is undefined if used in any
            other script than PCP.SCR.

                E.g.    send C @OUTBOUND,ABC12345<CR>


            @LOCALNUM

            Used to insert the local telephone number in a PC Pursuit script.
            The contents of @LOCALNUM is undefined if used in any other
            script than PCP.SCR.

                E.g.    send ATDT@LOCALNUM<CR>

        <C> @SYSTEMNUM

            Used to insert the telephone number of the system being called as
            if the Mailer or Terminal (if dialing a system listed in the
            nodelist) would have dialed the number.




                                         100




            ENDNODE

            Terminates a "node block". See NODE BLOCK.

        <C> UPLOAD <PROTOCOL> <FILESPEC>

            Transmits the files matching FILESPEC to the remote, using the
            PROTOCOL transfer protocol (X=Xmodem, T=Telink, S=SEAlink,
            Z=Zmodem). FILESPEC may include wild-cards characters for all
            protocols.

                E.g.    upload Z C:\FILES\FD*.LZH

        <C> DOWNLOAD <PROTOCOL> <PATH>

            Receives one or more files from the remote, using the PROTOCOL
            transfer protocol (X=Xmodem, T=Telink, S=SEAlink, Z=Zmodem). PATH
            must be a complete filename for Xmodem transfers and a valid
            directory for Zmodem, SEAlink, and Telink transfers.

                E.g.    download Z C:\INFILES\
                        download X C:\INFILES\FUN.LZH

        <C> DISCONNECT

            Unconditionally terminates a call (if any) from within a script.
            Script execution will resume as soon as the carrier (CD) signal
            has been lost; the script function lowers DTR to disconnect.

        <C> IFBAD
            <line to execute>

            Executes the command(s) listed on <line to execute> (which is the
            line following "IFBAD") if an UPLOAD or DOWNLOAD command failed. 

        <C> SENDBREAK

            Transmits a short BREAK signal to the modem.

        <C> LONGBREAK

            Transmits a long BREAK signal to the modem.

        <C> LINESPEED <BPS>

            Sets the baudrate the Mailer and Terminal use to determine
            transfer times, etc. to <BPS> BPS.

        <C> LOG <Symbol> <String>

            Adds <String> to the Mailer's log using the <Symbol> loglevel.







                                         101




            18.3 Labels

            A label is used to define a position in the script, so that it
            may be used as a jump destination. The label can consist of any
            word, starting with a letter from A to Z, except the above script
            commands, and must be preceded by a colon.

            At the position in the script where you want to execute a jump to
            the label, you enter the label name preceded by a greater than
            sign (>).

                E.g.    ..
                        ..
                        :redial
                        send ATDT@LOCALNUM<CR>
                        CASE
                            CONNECT     : session
                            BUSY        : >redial
                            @default    : fail
                        ENDCASE


            18.4 Node block

            A node block is a special type of label. It starts with a node
            number preceded by a colon. All commands from the first line to
            the ENDNODE statement, that ends the node block, will only be
            executed if you are currently calling the specified node.

                E.g.    ..
                        ..
                        :270/17         ; start of node block
                            send ATZ<CR>
                        ENDNODE         ; end of node block


            18.5 PC Pursuit

            You can use a generic script for calling all "PC Pursuitable"
            nodes, taking advantage of the specific PCP commands @OUTBOUND
            and @LOCALNUM. This requires that the script file is named
            PCP.SCR and is placed in the SYSTEM directory. You must also
            compile the nodelist with the file PCP.DAT, containing a list of
            all "PC Pursuitable" exchanges, present in the NODELIST
            directory.

            If you have followed these steps, the PCP script file will be
            used automatically when the Mailer detects that a node is "PC
            Pursuitable". You will probably want to prevent the Mailer from
            using the PCP script in the daytime on weekdays. A special route
            command, NO-SCRIPT, exists specifically for this purpose. For
            further information, see Mail routing.






                                         102




            18.6 How do I update PCP.DAT?

            The file PCP.DAT is a somewhat modified version of the file
            provided by Telenet's BBS. We take no responsibilities whatsoever
            regarding the contents of the PCP.DAT file supplied with
            FrontDoor. To update it, you must issue CONNECT PURSUIT from
            PCP's command prompt and log-on to their BBS. The file that you
            want to download is called EXCHANGE.TXT (or EXCHANGE.ARC). Should
            you update this file, you MUST make sure that your files follows
            the same format as the file supplied with FrontDoor.


            18.7 MNEMONICS

            The following mnemonics may be used to enter control characters
            in the script, both for sending and receiving. They can be used
            with the following commands: SEND, DIAL, PROVOKE, WAITFOR, and
            CASE.

                    ASCII    MNEMONIC   :   ASCII      MNEMONIC
                    --------------------+----------------------
                      0       <NUL>     :    17         <DC1>
                      1       <SOH>     :    18         <DC2>
                      2       <STX>     :    19         <DC3>
                      3       <ETX>     :    20         <DC4>
                      4       <EOT>     :    21         <NAK>
                      5       <ENQ>     :    22         <SYN>
                      6       <ACK>     :    23         <ETB>
                      7       <BEL>     :    24         <CAN>
                      8       <BS>      :    25         <EM>
                      9       <HT>      :    26         <SUB>
                     10       <LF>      :    27         <ESC>
                     11       <VT>      :    28         <FS>
                     12       <FF>      :    29         <GS>
                     13       <CR>      :    30         <RS>
                     14       <SO>      :    31         <US>
                     15       <SI>      :    32         <SP>
                     16       <DLE>     :
                    --------------------+----------------------


        19 FDSERVER <+>

        The Mailer has a function referred to as FDSERVER. It can be used to
        perform functions on your system from a remote site, such as moving
        and copying files, etc. FDSERVER is a very powerful function and the
        examples given in this chapter are only some of the things you can do
        with it.

        FDSERVER is activated by specifying a password in FDSETUP. FDSERVER
        requests will be ignored if no password has been specified in
        FDSETUP.

        FDSERVER requests are processed after a mail session has been
        completed and the call has been terminated, so everything you specify
        in request message is processed off-line.


                                         103




            19.1 What is a FDSERVER request?

            A FDSERVER request is a message, addressed to FDSERVER (case does
            not matter) on your system, with commands. Think of it as a
            remote, but controlled, DOS shell. You can run almost any program
            and perform any DOS function from a FDSERVER request. The
            FDSERVER function has some limitations, however.

                o   You cannot use the DOS command ECHO in a FDSERVER
                    request.

                o   Programs that require local keyboard input should not be
                    executed from a FDSERVER request since these program(s)
                    will just sit and wait for keyboard input.

                o   FDSERVER request messages must NOT be compressed
                    (ARCmail, etc.). The function is only triggered if the
                    Mailer unpacks the request message.

                o   Batch (.BAT) file labels are not supported.


            19.2 Request message

            Each line of the message is considered a command and blank lines
            are ignored. When FDSERVER has executed all commands found in the
            message, it will change drive and directory to where it was
            before processing your request and return to the Mailer.


                19.2.1 Internal commands

                Lines beginning with a % character are internal FDSERVER
                commands.

                    %logall

                    Will create one line in the log file for each command
                    that was executed along with the status (err: or exe:).

                    %nologer

                    Normally, all commands that generated an errorlevel will
                    be logged, this can be disabled with this command.

                    %store

                    After a request is processed, it will be deleted by
                    default. This can be disabled by putting this command in
                    the message which will force FDSERVER to mark the
                    messages as received.







                                         104




            19.3 Using it

            You are sitting in front of your computer at home, working with a
            report or something similar and find that you need some files
            from the office machine.

            Assuming that these files contain information that is very
            sensitive or confidential, and even though you have the option to
            protect your file requests with a password, you may still not
            want to have the files semi-accessible. This is where you can use
            FDSERVER.

            The directories and file names used in this example were thought
            up and does not necessarily match the setup on your machine.

            Create a message addressed to FDSERVER on the node you want to
            call and send it.

                By: joaquim homrighausen, JoHo's Home (2:270/17.1)
                To: fdserver, Use your illusion (2:270/17)
                Re: password
                ----------------------------------------------------
                %nologerr
                cd      \TEMP
                copy    C:\LOTUS\THA*.SPS

                arj a   THA THA*.SPS
                erase   *.SPS
                copy    THA.ARJ C:\REQUEST\FORNOW
                erase   THA.ARJ

            The server function will read the message and execute each line.
            The next step would be to create a new server request containing
            the following:

                By: joaquim homrighausen, JoHo's Home (2:270/17.1)
                To: fdserver, Use your illusion (2:270/17)
                Re: password
                ----------------------------------------------------
                %nologerr

                erase   C:\REQUEST\FORNOW\THA.ARJ

            And send it along with a File Request for THA.ARJ. The Mailer
            will process the File Request first, and when the mail session
            has been completed, the newly created server request will be
            processed by FDSERVER.


            19.4 Keeping calls to a minimum

            You could avoid the extra phone call in the example with the
            request if you have a robot utility such as XRobot and create a
            file attach with the files you need so the Mailer will call you
            back.



                                         105




            19.5 Security

            If you do not need to use FDSERVER, Do not define a password for
            it in FDSETUP. Since FDSERVER is a VERY powerful function, the
            results could be disastrous if someone got hold of your FDSERVER
            password.


        20 Service requests

        Service requests is a very powerful function of FrontDoor. It allows
        you to use the Mailer as a front-end to databases, to make on-line
        inquiries etc. without having to manually call the system with a
        Terminal program.


            20.1 Service requests vs FDSERVER

            The difference between a service request and a FDSERVER request
            is that they are processed while two systems are connected. This
            has the drawback of being slightly more expensive, but it offers
            a much greater flexibility than the FDSERVER function.

            Consider this. You have a program on your system that allows
            people to search for data in a database of files and then get a
            list of all the new files, you have named the service request
            WHATSNEW.

            Your system receives a file request for WHATSNEW and the Mailer
            invokes the program SEARCH.EXE, defined as the program to run for
            WHATSNEW. When SEARCH terminates, the Mailer will send the file
            NEWFILES.LST, created by SEARCH, to the remote system.


            20.2 Setting up

            Service requests are defined in the ALIAS file (where you define
            alias file names for file requests). The format of a service
            request definition looks like this:

                <NAME> ><PROGRAM> <PARAMETERS> ^<+ or - path name>

                E.g.

                WHATSNEW >SEARCH.EXE findit =A =T ^-C:\SERVICE\RESULT\*.TXT

            Service name

            NAME (case does not matter) is what the remote system should
            request to invoke the service request.

            Program

            >PROGRAM is the program that should be invoked when the Mailer
            receives a request for NAME. The > character is required and
            tells FD it is a service request and not an alias definition.
            There should be no spaces between the > and PROGRAM.

                                         106




            The extension of PROGRAM is important. The Mailer can execute
            batch (.BAT) files as a result of a service request, but it must
            do it through COMMAND.COM. So it has to know what type of file
            (program) it is that you are executing.

            Parameters

            You can pass any parameters to the program. The only restriction
            is (as with DOS) that they do not exceed a length of 128
            characters and none of them starts with the ^ (see below)
            character.

            There are several macros that you can specify as parameters.
            These macros are described in detail in the FrontDoor Developer's
            Kit (FDDEV).


            20.3 ^ - + ?

            The ^ character defines the beginning of a filemask that the
            Mailer should send after the service request has been completed.
            If no ^ definition has been made, the Mailer will not send any
            files as the result of a service request.

            The plus (+) means that the Mailer should NOT remove the files
            once they have been transmitted.

            The minus (-) means that the Mailer SHOULD remove the files once
            they have been transmitted. This also means that the files will
            be removed even if they could not be sent (carrier lost, etc).

            The question mark (?) means that the Mailer should ONLY remove
            the files once they have been SUCCESSFULLY transmitted. This
            means that if a session fails after transmitting three files,
            only those three files will be removed and the remaining left
            intact.

            The path name is a file specification, it may include wildcard (?
            and *) characters. The Mailer will send all matching files.


            20.4 Security

            Since service requests are built on the concept of File Requests,
            they are protected the same way a File Requests is protected. To
            setup a password, you have to use the Request Manager in FDSETUP
            and define a password for the service request name.


            20.5 A word of wisdom

            Service Requests should be used with extreme caution. It is
            recommended that you have a full understanding of what a service
            request actually does before you attempt to use it.




                                         107




            You should also keep in mind that the requesting system is
            waiting at the other end for the Mailer to start sending files.
            So keep it short and sweet.


        21 Global command-line switches

        Support for these switches is included in all programs in FrontDoor,
        except where otherwise stated. All command line parameters must be
        preceded by either a forward slash (/) or a dash (-). Command line
        parameters are case insensitive (case does not matter) except where
        otherwise stated. FD is the Mailer, FM is the Editor, and FDNC is the
        Nodelist Compiler.

        AUTOVIDEO   FM/FD   <C>

        Overrides the current video mode setting for the Editor and Mailer
        respectively.

        C           FDSETUP

        Forces color mode

        EMSIDEBUG   FD

        Enables extensive debug information when the Mailer negotiates a mail
        session using the EMSI protocol.

        FOLDER      FM      <C>

        Forces the Folder list to be displayed as soon as the Editor is
        invoked. This is identical to pressing <Alt-F> from the Editor's main
        menu.

        FOLDERSCAN  FM      <C>

        Similar to FOLDER (above) but emulates the behavior of <Ctrl-F>.

        FORCECOMMIT FD      <C>

        Forces the Mailer to flush the DOS disk buffers every time it writes
        data to disk while receiving a file. The use for this is to increase
        the integrity of received data, in case of a power failure. You can
        use it independent of the NOCOMMIT parameter, because the two are not
        related.

        FORCEDPMI   All

        Disables FrontDoor's autodetection of type of multitasker, and force
        time-slicing according to the DPMI-specification. OS/2 and Windows
        support DPMI.







                                         108




        FORCEINT28  All

        Force FrontDoor to issue INT 28H calls when it is idle. This is
        useful in such multi-tasking environments which support this method
        for applications to give up time slices (most notably older TSR
        programs written to run in the background).

        INTL        FM

        Forces the Editor to always insert the ^aINTL kludge line in newly
        created NetMail messages. The Editor will, by default, only insert
        INTL information if the destination system of the message is located
        in a different zone than that of the originating address (your) used
        to create the message, or when a different originating address than
        your primary AKA is used.

        L:<pwd>     FD

        Locks the keyboard with the specified password directly from DOS.
        This has the same effect as using the Lock, <Alt-L>, function from
        the Mailer's main menu.

        LOGINTRO    FD

        Enables more detailed information to be logged during the initial
        phase of a mail session negotiation.

        M           FDSETUP

        Forces monochrome mode

        M           FD

        Forces the Mailer into Mail mode directly from DOS. This switch was
        added to allow you to override the Terminal-only setting in FDSETUP.

        MSGSURVEY   FM      <C>

        Forces the Message Survey function to be selected as soon as the
        Editor is invoked. This is identical to pressing <Alt-F9> from the
        Editor's main menu.

        NOCANSES    FD      <C>

        Forces the Mailer to ignore the FDCANSES.n semaphore.

        NOCOMMIT    All

        Disables use of DOS 3.3 commit() call.

        NODASH      FD

        Forces the Mailer and Terminal to strip dash (-) characters from
        telephone numbers before sending them to the modem. This does not
        affect how telephone numbers are displayed on screen or logged to
        disk.


                                         109




        NODUPBCK    FDSETUP

        Disables the duplicate Hudson Message Base board check that FDSETUP
        normally performs when you edit and add Folders in the Folder
        manager.

        NOEKBD      All

        Prevents FrontDoor from using extended (AT-style) keyboard BIOS
        calls.

        NOEMS       All

        Disables use of LIM/EMS memory for overlay file buffers. This switch
        does not affect whether or not EMS/XMS memory is used when (if)
        swapping.

        NOEMSI      FD

        Disables support for the FSC-0056 (EMSI) session protocol. This means
        that the Mailer will only support FTS-1 and FTS-6 sessions, unless
        otherwise restricted.

        NOFCB       FD

        Disables the use of the File Control Block (FCB) delete function when
        the Mailer shall remove files in the Packet directory. Its intended
        use is for dealing with special incompatibilities, such as with the
        "DELDIR" setting of OS/2 2.0. It is likely to impose a decrease in
        speed when the Mailer is processing mail packets.

        NOFTSC1     FD

        Disables support for the FTS-1 session protocol, effectively making
        the Mailer non-FidoNet compliant. This means that the Mailer will
        only support FTS-6 and EMSI sessions, unless otherwise restricted.

        >>> Public (listed as non-PVT in the FidoNet nodelist) FidoNet
            systems should use this option with CAUTION since by using it,
            you may be in violation FidoNet policy.

        NOICA       FM/FD

        Prevents the Editor and the Mailer from using the ICA (intra-
        application communications BIOS area). Some combinations of hardware
        and software (notably in some Gateway brand of PCs with specific BIOS
        revisions) have problems with the support of ICA-enabled
        applications.

        NOISCR      FM

        Forces the Editor to treat a SoftCR (ASCII 141) character as any
        other printable character. The default for the Editor is to strip
        these when reading and writing message from/to disk.




                                         110




        NOLOCK      FM

        Disables Hudson Message Base locking support in the Editor. Do not
        use this unless absolutely necessary.

        NOMDM       FD

        Forces the Mailer to ignore information listed in MODEM.FD.

        NOMULD      All

        Prevents FrontDoor from attempting to detect a multi-tasking
        environment, such as DESQview and PC-MOS/386.

        NORAWEXTD   FD

        Forces the Terminal to send the normal (white) cursor key sequences
        when the gray cursor keys are used in raw keyboard mode (Scroll Lock
        is enabled). This may be required by some "doorway" programs that do
        not support extended keyboard codes.

        NORES       All

        Disables use of internal DOS pathname resolution calls. This is
        required under PC-MOS/386 and some LAN environments.

        NORESYNC    FD

        Disables support for the RESYNC extension to the SEAlink protocol.

        NOSHADOW    All

        Disables window shadows.

        NOSLO       FD

        Disables support for the Overdrive protocol option (SLO) in SEAlink.
        SLO is by default only active during "error free" connections (/ARQ,
        /MNP, /LAPM, etc.) and for link speeds above 2400 BPS.

        NOUNPACK    FD

        Forces the Mailer to ignore received mail packets (files with .PKT
        extension). This assumes that you have an external utility to unpack
        NetMail packets. Do not use this unless you absolutely need it.

        NOYOOHOO    FD

        Disables support for the FTS-6 (YooHoo) session protocol. This means
        that the Mailer will only support FTS-1 and EMSI sessions, unless
        otherwise restricted.







                                         111




        NOZAP       FD

        Disables support for the Zmodem protocol during mail sessions
        negotiated using the FTS-6 (YooHoo) session protocol. This
        effectively means that the Mailer will only establish FTS-6 sessions
        using the DietIFNA protocol option. This does not affect sessions
        negotiated using EMSI.

        ONLINE      FD      <C>

        Forces the Terminal to not initialize the modem when it is started.

        RDEBUG      FD

        Enables debug output from the mail routing handler in the Mailer.
        This is quite useful when debugging your ROUTE.FD file.

        S           FD

        Forces the Mailer to ignore any forced events it may have missed. The
        Mailer will by default execute all pending external events when it is
        brought up. This switch is useful if you have performed system
        maintenance for several hours and do not want overdue forced events
        to be executed.

        SESSONDCD   FD      <C>

        Forces the Mailer to immediately attempt to initiate a mail session
        when the DCD (carrier) signal goes high.

        TERM        FD

        Forces the Mailer into Terminal mode directly from DOS. Once you exit
        the Terminal, you will be returned to DOS.

        X<1..255>   FD      <C>

        Forces the Mailer to terminate with the specified errorlevel as soon
        as there is no more outbound calls to make.


            21.1 A word of wisdom

            Please be aware that some of the previously described command
            line switches completely alter the way FrontDoor acts and may
            make it incompatible with other software and/or some
            environments.

            Use the switches with caution and when in doubt, try to test the
            effects of the switch in a local environment or between your own
            and a friend's system before you leave the Mailer to answer your
            telephone unattended.






                                         112




        22 Environment variables

        Several environment variables affect how FrontDoor operates. It is
        assumed that you are familiar with what and environment variable is
        and how to set/remove one.


            22.1 FDOPT

            All of the "Global command line switches" except -C and -M can
            also be specified by including them in the FDOPT environment
            variable. To include more than one option, separate them by a
            comma, e.g.

                SET FDOPT=NOISCR,NOSHADOW


            22.2 FDSWAP

            Overrides the "Swapping" path, defined under Global > Filenames
            in FDSETUP, e.g.

                SET FDSWAP=D:\TEMPDIR\


            22.3 POINTNET

            See "Nodelist and the Nodelist Compiler".


        <C> 22.4 FMOVR and FDOVR

            Allows you to specify a complete path where the Editor and the
            Mailer should look for their overlay (.OVR) files. Useful when
            multiple copies of either program are being used (e.g. multi-line
            environment).


            22.5 TZUTC

            Allows you to specify your geographical time zone's offset to UTC
            (GMT) time. E.g.

                SET TZUTC=[-|+]hhmm

            The plus-sign (+) is optional, meaning that the use of SET
            TZUTC=0100 and SET TZUTC=+0100 would both indicate that your time
            zone is Paris (Central European Time), which is one hour east of
            GMT (Greenwich Mean Time). The Editor will insert the TZUTC
            kludge if the environment variable is present. The Mailer will
            present the TZUTC-setting during EMSI handshakes, <C> and as a
            kludge when creating return receipts.

            If you periodically change your system clock according to
            "summer/winter time", you will need to adjust the setting of
            TZUTC as well. Here follows a list of some of the world's time
            zones:

                                         113




                Zone    Offset  Name
                ------------------------------------------------
                AHST    -1000   Alaska-Hawaii Standard Time
                HDT     -0900   Hawaii Daylight Time
                PST     -0800   Pacific Standard Time
                PDT     -0700   Pacific Daylight Time
                MST     -0700   Mountain Standard Time
                MDT     -0600   Mountain Daylight Time
                CST     -0600   Central Standard Time
                CDT     -0500   Central Daylight Time
                EST     -0500   Eastern Standard Time
                EDT     -0400   Eastern Daylight Time
                WAT     -0100   West Africa Time
                GMT     +0000   Greenwich Mean Time
                UTC     +0000   Universal Time
                CET     +0100   Central Europe Time
                BST     +0100   British Summer Time
                CEST    +0200   Central Europe Summer Time
                EET     +0200   Eastern European Time
                WAST    +0700   West Australian Time
                WADT    +0800   West Australian Daylight Time
                CCT     +0800   China Coast Time
                JST     +0900   Japan Standard Time
                CAST    +0930   Central Australian Standard Time
                EAST    +1000   East Australian Standard Time
                CADT    +1030   Central Australian Daylight Time
                EADT    +1100   East Australian Daylight Time
                NZST    +1200   New Zealand Standard Time
                NZDT    +1300   New Zealand Daylight Time


        23 Semaphore files

        FrontDoor can be controlled by using so called semaphore files. Both
        the Mailer and the Editor periodically scan for certain file names in
        the SYSTEM directory, and if found, performs a task such as
        rescanning the contents of the NetMail folder, exits to DOS, prevents
        human callers, and more.

        <C> The commercial version furthermore allows you to specify a
        separate semaphore directory (see FDSETUP > Global > Filenames) to
        allow several copies of the Editor and the Mailer to use the same
        semaphore files.

        The Mailer uses the lower right hand corner of its main screen to
        indicate that some semaphore files are present. FD is the Mailer and
        FM is the Editor.

        FMRESCAN.NOW    FM

        Forces the Editor to rebuild its internal list of messages in the
        NetMail folder.






                                         114




        FMFREEZE.n      FM      <C>

        Used to freeze task(s) running the Editor. The Editor will search for
        this semaphore once a minute, when updating the on-screen clock. When
        found, the keyboard is frozen, the databases for nodelist and
        messages are closed, and the Editor will check every twenty seconds
        to see if the semaphore has disappeared. FMFREEZE.ALL has a similar
        function but affects all currently active Editors rather than just
        the specified task.

        FMNEW???.n      FM      <C>

        Created by the the Editor to indicate that new messages (including
        replies) have been entered as NetMail, conference mail, and local
        mail respectively. The classification of messages is defined by the
        settings under Manager > Folders in FDSetup, of the corresponding
        folder(s) where one or more new messages have been saved. You can
        control support of these semaphores in FDSetup, under the Editor >
        Miscellaneous menu. Messages saved with the Lock attribute are not
        considered as new. The actual names are FMNEWCNF.n, FMNEWNET.n, and
        FMNEWLOC.n respectively.

        FDRESCAN.NOW    FD

        Forces the Mailer to discard all mail packets from the packet
        directory and rescan the contents of the NetMail folder before
        rebuilding the packets.

        FDINSESS.nnn    FD/FM   <C>

        The Mailer creates this file whenever a mail session is initiated,
        and when it is dialing a system, attempting to establish a mail
        session. If the Editor detects this file, it will not let you
        renumber the NetMail folder. "nnn" is the task number (0-255).

        FDINEXIT.nnn    FD

        The Mailer creates this file whenever a human caller is detected and
        passed onto a BBS or other interactive service. When the Mailer is
        restarted, it compares the timestamp of FDINEXIT.nnn with the
        timestamp of FDRESCAN.NOW, and if they do not match, a complete
        rescan (see above) is performed. "nnn" is the task number (0-255). In
        the shareware version, this file is not task aware, and is always
        called "FDINEXIT.NOW".

        FDFREEZE.n      FD      <C>

        Used to freeze task(s) running the Mailer. The Mailer will search for
        this semaphore once a minute. When found, the keyboard is frozen, the
        nodelist database and the log file is closed, and the Mailer will
        check every twenty seconds to see if the semaphore has disappeared.
        FDFREEZE.ALL has a similar function but affects all currently active
        Mailers rather than just the specified task.





                                         115




        FDNOUSER.NOW    FD

        Forces the Mailer to refuse human callers. This has the same effect
        as setting the "Human callers" option, under FD's "Your profile"
        menu, to "NO". The visual indicator for this semaphore file is "NU".

        FDNOSCAN.NOW    FD

        Forces the Mailer to ignore FDRESCAN.NOW.

        FDNOEXIT.NOW    FD

        Prevents the Mailer from exiting because of received mail. This has
        the same effect as setting the "Exit on mail" option, under the "Your
        profile" menu, to "NO". The visual indicator for this semaphore file
        is "NE".

        NODIAL.FD       FD

        While this is not a semaphore file per se, it triggers the display of
        a visual indicator, "UD".

        FDEXIT.nnn      FD

        Forces the Mailer to unconditionally exit with the errorlevel "nnn".
        Before it exits, the Mailer removes the file.

        FDRENUM.nnn     FD/FM   <C>

        The Editor creates this file whenever you press <Alt-B> to renumber
        the NetMail folder. When the Mailer detects this file, it will not
        place any outgoing calls until it can no longer be found. This
        prevents the Mailer from initiating an outbound session while the
        Editor is renumbering the contents of the NetMail folder. "nnn" is
        the task number (0-255).

        ROUTE.FD        FD

        While this is not a semaphore file per se, it is used to determine if
        the NetMail folder has to be rescanned (see above). If the timestamp
        of this file has changed since the Mailer last checked it, a rescan
        is forced.

        FDALIVE.n       FD      <C>

        Used by the Mailer to indicate that it is still "alive". The
        timestamp is updated every few minutes even when the Mailer has been
        frozen with the FDFREEZE semaphore, or when the Terminal is active.
        It provides a simple method to monitor whether or not the Mailer is
        operating as it should. When the Mailer terminates, or a DOS shell is
        invoked, the semaphore is removed.







                                         116




        FDSCAN.n        FD      <C>

        Used to indicate that the Mailer is processing the (primary) NetMail
        folder. While this semaphore is present, certain functions in the
        primary NetMail folder (such as renumber and change of destination)
        are disabled in any task running the Editor.

        FDINTERM.n      FD

        Created and present for the duration when the Terminal is running. In
        the shareware version, this file is named FDINTERM.NOW.

        FDCANSES.n      FD      <C>

        Used to force the Mailer to terminate the currently active session.
        The semaphore is checked for between files being sent/received. If
        the Mailer finds the file, it removes the file and terminates the
        session. The Mailer can be told to ignore this file by using the
        NOCANSES option as described above.


        24 Batch files

        The Mailer will, in most cases, be run from a DOS batch (.BAT) file.
        When it terminates, it will return certain errorlevels that you can
        "trap" for in your batch file.


            24.1 Errorlevels

                1           Internal error
                2           External error - missing files, paths, etc.
                3           Insufficient available disk space (less than 32
                            KB)
                4           (reserved)
                5           Unable to initialize modem
                6           Incorrect FOSSIL version
                7           FOSSIL not loaded or detected
                8           FrontDoor already loaded, issue EXIT to return
                9           (reserved)
                10          User break
                11 - 30     (reserved)
                31 - 255    User definable errorlevels

            If you invoke the Terminal from DOS by running FD /TERM, it will
            always terminate with an errorlevel of 10 (User break), the same
            applies when you have specified "Terminal-only" in FDSETUP.


            24.2 Categories

            The various errorlevels can be organized into four basic
            categories:





                                         117




                Mail received

                When mail is received, you can choose to exit to the batch
                file to run external mail processing utilities, such as
                TosScan, etc.

                User break/errors

                When you press <Alt-Q> from the Mailer's main menu or when
                errors occur.

                BBS calls

                If you are running a BBS under the Mailer, it must exit with
                an errorlevel indicating the baudrate of the call. The line
                is still active when the Mailer exits to the batch file, the
                BBS software is loaded, and the caller will be able to access
                the BBS.

                External events

                The errorlevels defined in FDSETUP's event manager.


            24.3 Loading BBS software

            There are two methods that can be used to invoke BBS software
            when the Mailer detects an interactive call. The first uses
            different batch file labels for the various baudrates and the
            second one uses the same label for the various baudrates. The
            second method relies on the "Create .BAT file" option in FDSETUP
            (under Mailer > Errorlevels).


            24.4 Different labels

            @echo off
            rem            --- We end up here after every BBS call
            :loop

            C:
            CD \FD
            FD

            rem            --- Check errorlevels returned by the Mailer

            if errorlevel 200 goto b9600
            if errorlevel 199 goto b2400
            if errorlevel 198 goto b1200
            if errorlevel 197 goto b300
            if errorlevel 100 goto mailIN
            if errorlevel  10 goto userBRK
            if errorlevel   1 goto FDerror

            :mailIN

            rem            --- Process possible echomail, etc.

                                         118




            tosscan toss
            tsutil link -m
            goto loop

            :b9600

            Load BBS software for incoming call at 9600 bps
            goto loop

            :b2400

            Load BBS software for incoming call at 2400 bps
            goto loop

            ..
            ..

            :userBRK
            cls
            @echo     User break.
            goto      done

            :FDerror
            @echo     Mailer returned an error (1-9)

            :done

            While this option works just fine for a environment where it is
            not critical that the BBS software knows about upcoming events
            etc. it is somewhat limited.


            24.5 Same label

            @echo off
            rem            --- We end up here after every BBS call
            :loop

            C:
            CD \FD
            FD

            rem            --- Check errorlevels returned by the Mailer

            if errorlevel 200 goto bbsCALL
            if errorlevel 199 goto bbsCALL
            if errorlevel 198 goto bbsCALL
            if errorlevel 197 goto bbsCALL
            if errorlevel 100 goto mailIN
            if errorlevel  10 goto userBRK
            if errorlevel   1 goto FDerror

            :mailIN

            rem            --- Process possible echomail, etc.

            tosscan toss

                                         119




            tsutil link -m
            goto loop

            :bbsCALL
            rem            --- Load DOBBS.BAT, created by the Mailer if
            rem                the "Create .BAT file" option is enabled.
            dobbs

            :userBRK
            cls
            @echo     User break.
            goto      done

            :FDerror
            @echo     Mailer returned an error (1-9)

            :done


            24.6 DOBBS.BAT

            This is the batch file created by the Mailer when you have the
            "Create .BAT file" option enabled. It contains the speed at which
            the call came in, the COM port, number of minutes left until the
            next event and possibly a string indicating ARQ, MNP etc.
        <+> Additionally, the registered version can include data following
            the ring signal (DFRS), i.e. CALLER*ID information.

            For a call coming in at 16800 BPS with ARQ, with 30 minutes left
            until the next non-user event, on COM port 1, and with no DFRS
            the DOBBS.BAT file would contain:

                exebbs 16800 1 30 0 /ARQ N/A

            For a call coming in at 2400 BPS, with two hours left until the
            next non-user event, on COM port 1, the DOBBS.BAT file would
            contain:

                exebbs 2400 1 120 0 /NONE N/A

            The parameter between the remaining time and possible extended
            modem result code information (e.g. /ARQ, /MNP, etc.) is the task
            number and is always zero for the shareware version. If the modem
            did not send any extended result code information (other than a
            "CONNECT nnnn"), the Mailer will insert /NONE.


            24.7 EXEBBS.BAT

            This is the file you have to create. It should handle everything
            required for the BBS software you are running, including
            exporting mail after users have logged off, etc. The last
            statement of your EXEBBS.BAT file should be the name of the big
            (main) batch file. Here is a sample of an EXEBBS.BAT file:

                coolBBS -b%1%5 -p%2 -t%3


                                         120




                if errorlevel 200 goto newmail
                if errorlevel 40  goto fatal

                run

                :newmail
                cls
                @echo User entered echomail, let's send it!
                tosscan scan
                run

                :fatal
                cls
                @echo A fatal error has occurred in coolBBS

                Since DOBBS.BAT calls EXEBBS.BAT with various information, it
                can be used to pass parameters to the BBS software. The
                result of the above EXEBBS.BAT file would expand to:

                    coolBBS -b9600/ARQ -p1 -t120

                If a BBS call came in at 9600, the COM port is one, the
                number of minutes till the next non-user event is 120 and the
                optional (%5) string contained /ARQ.

                The text RUN, refers to the original (main) batch file, in
                which we bring the Mailer back up again. When the BBS
                software (coolBBS in the above examples) terminates,
                EXEBBS.BAT will trap two errorlevels and then invoke
                RUN(.BAT) again.


            24.8 Flow (batch files)

            Complicated? Here is the actual file flow between RUN, DOBBS and
            EXEBBS:

                +-> RUN.BAT     Loads the Mailer and performs all EchoMail 
                :     :         and error handling. When an interactive (BBS)
                :     :         call is detected, it loads DOBBS.BAT,
                ^     V         created by the Mailer.
                ^     :
                :     :
                :  DOBBS.BAT    Created by the Mailer. DOBBS calls EXEBBS.BAT
                :     :         file with the parameters relevant for the
                :     :         incoming call.
                ^     V
                ^     :
                :     :
                :  EXEBBS.BAT   Called by DOBBS.BAT with the above described
                :     :         parameters. Loads the BBS software, processes
                ^     :         newly created mail (if any), and finally
                ^     V         returns to RUN.BAT.
                :     :
                +--<--+



                                         121




        25 Multi-tasking

        FrontDoor can be used together with most multi-tasking programs. It
        has been tested with DESQview, PC-MOS/386, OS/2 1.3, 2.0, and 2.1 DOS
        Box, DoubleDOS, Multilink, Windows, Windows NT, and Taskview. It will
        automatically detect most multi-tasking software.


            25.1 NS16550

            If you are running FrontDoor under a multi-tasker or in a LAN
            environment, I suggest you replace your 8250 or 16450 UART chip
            with a NS16550AN or NS16550AFN. These are available from several
            electronics outfits for somewhere between USD 17 and USD 23.

            The 16550 family of UARTs have internal buffering (FIFO) and will
            improve performance in multi-tasking and LAN environments. Both
            BNU and X00 has direct support for the 16550 family and can be
            used without modifying your command-line parameters when loading
            them.


            25.2 DESQview

            FrontDoor will request a virtual screen buffer from DV and write
            to it. The result is very fast and very well behaved screen
            writes. Here's a sample DESQview configuration:

                Keys to Use on Open Menu            FD
                Memory Size (in K)                  270

                Options:

                Writes text directly to screen      N
                Displays graphics information       N
                Virtualize text/graphics (Y,N,T)    N
                Uses serial ports (Y,N,1,2)         2
                Requires floppy diskette            N

                Advanced Options:

                System Memory (in K)                0
                Maximum Program Memory Size (in K)  <empty>
                Script Buffer Size                  0
                Maximum Expanded Memory Size (in K) 0

                Text Pages                          1
                Graphics Pages                      0
                Initial Mode                        <empty>
                Interrupts                          00 to FF

                Maximum Height                      25
                Starting Height                     25
                Starting Row                        1
                Maximum Width                       80
                Starting Width                      80
                Starting Column                     1

                                         122




                Close on exit (Y,N,blank)           N
                Uses its own colors                 Y
                Allow Close Window command          Y
                Runs in background (Y,N,blank)      Y
                Uses math coprocessor               N
                Keyboard conflict (0-4)             0
                Share CPU when foreground           Y
                Share EGA when foreground/zoomed    Y
                Can be swapped out (Y,N,blank)      N
                Protection level (0-3)              0


            25.3 DoubleDOS

            Smart multi-tasking software allocates a virtual screen buffer
            for each task. Applications can then ask the multi-tasking
            software where it should write and the multi-tasker handles the
            screen updates. DoubleDOS 5.0 uses a different method.

            Every time you switch tasks from the keyboard, the screen-buffers
            change. So there is no easy way for the software running under
            DoubleDOS to detect this. In DoubleDOS 5.00, there are two
            options that allows you to run FrontDoor under DoubleDOS just
            fine. You MUST run FrontDoor in the TOP section for the two
            methods below to work.


                25.3.1 DISPLAY=TEXT

                If your system has a MCGA, CGA, EGA or VGA card installed,
                there is extra memory available on those cards for graphics,
                etc. DoubleDOS can use some of that memory for each of its
                screen buffers. To enable this, add DISPLAY=TEXT to your
                DDCONFIG.SYS file.


                25.3.2 REFRESH

                If you have a text-only adapter (MDA) there is most likely no
                extra memory available on the card. Add REFRESH by itself on
                a line to your DDCONFIG.SYS file. This will tell DoubleDOS to
                repaint the screen if the other task is bleeding through.


                25.3.3 X00 and DoubleDOS

                When using FrontDoor, X00.SYS, and DoubleDOS, do not assign
                the COM ports in DDCONFIG.SYS. If you have problems with your
                clock, try the DEFER option in X00.

            Make sure you replace ANSI.SYS with DBLDANSI.SYS.

            The BOTTOM partition should initialize before the TOP partition.
            In other words, if you are loading FrontDoor in the BOTTOM
            partition, try to delay the initialization of the TOP partition.



                                         123




            25.4 Multilink

            I would personally not recommend anyone using FrontDoor with
            Multilink. I have never successfully executed any program under
            Multilink for longer periods of time than momentarily.


        26 Converting from other mail systems

        If you were using SEAdog or D'Bridge before you started using
        FrontDoor, you should have little trouble converting to FrontDoor.
        The routing and message handling used by these two mail systems is
        very similar to the way things are done with FrontDoor.

        If you are converting from BinkleyTerm, Opus, or Dutchie, however,
        there are a few things you should know and make sure you have done
        before you install FrontDoor.

        The main difference between FrontDoor and BinkleyTerm or Opus is that
        FrontDoor does not use oMMM, i.e. a static message packer. I see the
        oMMM approach as a black hole from which there is no return. This is
        not true in some cases and there are advantages of using oMMM type
        packers instead of the method used by FrontDoor.

        oMMM will create static bundles, where each system has a control file
        that tells the Mailer what files and messages to send to what
        systems. FrontDoor will NOT recognize oMMM type bundles (packets) so
        before you fully convert to FrontDoor, you must make sure that all
        the oMMM type mail is sent before you convert to FrontDoor.

        You can use FrontDoor to send the remaining oMMM type mail by
        attaching the files manually with FrontDoor's Editor or a robot
        utility such as XRobot, but you will need a utility with which you
        can determine which file belongs to which system before you can do
        this. So it might be easier for you to tell BinkleyTerm or Opus to
        send its remaining mail before you do the conversion.


        27 Help systems

        For a list of help systems that can help you with problems that you
        encounter with the shareware versions, please refer to the file
        FDHELPnn.TXT that is distributed in the FidoNet SDSFRONT file
        conference. If all else fails, contact either Bruce Bodger on
        1:170/400@fidonet, or Mats Wallin on 2:201/329@fidonet. The official
        FidoNet support conference for the shareware version is FDECHO.

        Please note that the FidoNet help systems are not responsible for
        giving support to users of the commercial version of FrontDoor.
        Likewise, commercial suppliers of FrontDoor are not responsible for
        giving support to users of the shareware version of FrontDoor.

        If you have purchased the software with the SysOp discount, you may,
        however, post your questions in FDECHO. For shareware registration
        information, please refer to the REGINFO.DOC file enclosed in the
        distribution archive.


                                         124




        28 Sample (PCP) script

        ; PCP script for FrontDoor version 2.11
        ; Eric Larson, 1:2605/620.0, 8/11/91
        ; Modified from script supplied in FD 1.99 documentation
        ;
        ; Joaquim Homrighausen makes no claims of the accuracy, nor
        ; does he take any responsibility for the information provided
        ; in this file.
        ;
        ; You must modify this script in at least 3 places:
        ;
        ;   1: Indial Number
        ;   2: PCP ID Number
        ;   3: PCP Password
        ;
        ; You may also want to modify the script for your modem
        ; or types of systems you call. See notes in script.
        ; For further information, see PCP documentation on
        ; Net Exchange BBS. To connect to the Net Exchange, type
        ; "C PURSUIT" at the Telenet @ prompt.
        ;

        debug     ON
        setport   2400          ; Redundant if you have locked your FOSSIL
                                ; If you have a 1200 indial :-(, use 1200
                                ; here and change the hunt-confirm sequence
                                ; to @ wait 1 <CR>
        ;
        ; Users with MNP modems should disable MNP as the buffering
        ; combined with PCP's packet latency will cause block position
        ; errors during error recovery. For HST owners, use:
        ;
        send AT&M0<CR>
        waitfor OK
        ;
        ; Others should adjust the above for their modem
        ; non-buffered modem owners should comment out the
        ; above two lines.
        ;
        ;----------------------------------
        ; Your Indial Phone Number Here
        ;----------------------------------
        ;
        send ATDT4795372<CR>
        ; send ATDT4795445<CR>                      ; official number
        ; 6406 5776 5355 5372                       ; alternates
        ;
        ; If you are having difficulty with your indial line, call
        ; PCP customer service and they may be able to give you
        ; an alternate number that works better.







                                         125




        case
             CONNECT        : >whackit
             RING<CR>       : fail
             BUSY<CR>       : fail
             "NO "          : fail
             @default       : fail
        endcase

        :whackit                    ; Attempt to "wake-up" PCP
             purgein                ; Telenet recommends at least
             wait      2            ; a 200 ms pause between
             send      @            ; characters in the hunt-confirm sequence
             wait      1            ; change the @ to <CR> if you call        
             send      D            ; a 1200 bps indial
             wait      1
             send      <CR>
             waitfor   TERMINAL=
             send      D3<CR>       ; Preferred terminal type
             waitfor   @

        ;--------------------------
        ; Your ID and Password Here
        ;--------------------------

        :outdial                    ; Dial PCP city
             purgein
             retrycount 5
             send      C @OUTBOUND,YOURID471E<CR>   ; Your ID Here
             waitfor   PASSWORD
             send      KKKKKK<CR>                   ; Your Password Here

        CASE
             CONNECT         : >local               ; Gotcha!
             BUSY            : >outdial
             "NOT "          : fail
             @nocarrier      : fail
             @default        : fail
        ENDCASE

        :local                                      ; Initialize Outdial
             purgein
             send <CR>
             wait 1
             send I<CR>
             send ATZ|
             timerset 15
             waitfor OK
             send @|
             waitfor @
        ;
        ; Setup PADS
        ;
        ; Note - if you are calling a SEAdog system,
        ; change the SET and RST 5:1 and 12:1 to 5:0 and 12:0
        ; as SEAlink is not transparent to software flow control



                                         126




        ;
        ; If you only call WaZoo systems, use 5:1 and 12:1 for
        ; fewer errors and greater reliability.
        ;
        send SET?<sp>1:0,7:8<CR>
        ;
        waitfor @
        ;
        ; send RST?5:1,12:1<CR>
        ;
        ;    waitfor @

             send CONT<CR>
             send ATH0Z<CR>
             waitfor OK|IDLE
             send <ENQ><CR>                ; Turn on RV Mode
             waitfor *

             purgein

             timerset 50
             wait 2
             send D@LOCALNUM<CR>

             purgein

        case
             ANS             : >landing
             ONLINE          : >landing
             BUSY            : fail
             FAILED          : fail
             "NO CARRIER"    : fail
             "NO DIAL TONE"  : fail
             "NO DTR"        : fail
             VOICE           : fail
             @default        : fail
             @nocarrier      : fail
        endcase

        :landing                           ; Landing on Pluto
             wait 7                        ; wait for PCP messages to clear   
          purgein
             session

        ;end of file "pcp.scr"


        29 Commercial inquiries

        For any use other than that allowed by the licence agreement, you
        must obtain the commercial version of FrontDoor. The commercial
        version of FrontDoor include numerous features not found in the
        shareware version. Eligible users of the shareware version of
        FrontDoor may also benefit from the commercial features, and can
        enjoy a special "SysOp Discount" at the time of this writing.



                                         127




        The easiest way to receive up-to-date information of features,
        availability, pricing and a list of local distributors and resellers
        of the commercial version, is to file request FDINFO from one of the
        following main distribution sites:

            Online Communications, Inc.     Telephone:  +1 207 941 1110
            22 State Street                     Modem:  +1 207 990 3511
            Bangor Maine 04401                    Fax:  +1 207 990 2293
            USA                                 Email:  1:132/300@fidonet

            ComDas GmbH                     Telephone:  +49 911 970 780
            attn: Holger von Heissen            Modem:  +49 911 970 7821
            Hornschuchpromenade 28                Fax:  +49 911 707 104
            D-90762 Fuerth                      Email:  2:247/1808@fidonet
            Germany

        FDINFO is also available from 2:270/17@fidonet.

        The FDINFO package contains information about various FrontDoor-
        related utilities, such as TosScan, the conference mail package.


        30 Developer notes

        A separate package with information regarding FrontDoor is
        distributed under the name FDDEV. It contains structures and
        technical information directed towards authors of FrontDoor
        utilities. If you are planning on writing a utility with explicit
        support for FrontDoor, make sure you grab a copy of the FDDEV
        package.


        31 Technical specifications

        FrontDoor was written using Zortech C++ 3.1, TASM 2.0, and Turbo
        Pascal 6.0. It uses direct-to-screen writes, and properly supports
        virtual screen environments, such as the one provided by DESQview.

        FrontDoor's FTSC product code is 0x0C (or 12 decimal).

        The proper nodelist flag for file requests for systems using
        FrontDoor is XA.

        FrontDoor's Editor allows you to share the Hudson Message Base
        together with other programs, such as RemoteAccess, following the
        RemoteAccess/FrontDoor HMB sharing specifications.


        32 Credits

        This list, as most lists, started out in 1986 with a few names. It
        has since grown to unrealistic proportions and instead of running the
        risk of forgetting to mention someone, I'll take the cheap way out
        and say thanks to everyone who has contributed to making FrontDoor
        what it is today. You know who you are.

        I do wish to point out a "few" people though..

                                         128




        .. the beta crew, the help nodes, all you people who keep pestering
        me with NetMail about things that you want to see in FrontDoor, Ron
        Dwight, Peter Garben (1111), all the people who turned up at EuroCon
        '93, M.E., C.A., G.A., THA/2, Lill Homrig, Senior, the JAM crew..

        And last, but not least..

        ..Tom Jennings, Felix Kasza, Bob Hartman, Chris Irwin, Chuck
        Forsberg, Henk Wevers, Randy Bush, Ray Gwinn, Thom Henderson, Vince
        Perriello, Wynn Wagner III, Mike Ratledge, Rick Moore, G. Adam
        Stanislav, Doug Boone, Ralf Brown, jim nutt, Maximilian Hantsch,
        Alexander Holy, Scott Dudley.


                       "It ain't over till the fat lady sings"











































                                         129




        Batch files  117                         NOLOCK  111
            BBS  118                             NOMDM  111
            CALLER*ID  120                       NOMULD  111
            Create .BAT file  16,                NORAWEXTD  111
                118, 120                         NORES  111
            DOBBS.BAT  120                       NORESYNC  111
            Errorlevels  16, 47, 117             NOSHADOW  111
            EXEBBS.BAT  120                      NOSLO  111
            FDEXIT semaphore  116                NOUNPACK  111
            FDNOEXIT semaphore  116              NOYOOHOO  111
            Flow  121                            NOZAP  112
            Mail received  118                   ONLINE  112
            Terminal  117                        RDEBUG  112
            TZUTC  113                           S (Mailer)  112
            X<1..255>  112                       SESSONDCD  112
        BBS                                      TERM  21, 68, 112, 117
            DOBBS.BAT  120                       X<1..255>  112
            EXEBBS.BAT  120                  Commercial inquiries  127
            Human callers (mailer            CONFIG.SYS
                profile)  54                     BUFFERS=  4
            Loading  13, 118                     FILES=  4
            Mail only  12                    Credits  128
            Maximus  83                      Display
            RemoteAccess  83                     "Mail"  14
            Software  4                          "NE"  116
        Carbon copies  66                        "UD"  116
            Blind  67                            <C> and <+>  3
            Hidden  67                           AUTO  84
        Command-line parameters  108             AUTOVIDEO  108
            AUTOVIDEO  108                       C command-line parameter 
            C (FDNC)  34                             108
            C (FDSETUP)  108                     Clear screen  72
            DOBBS.BAT  120                       Clock  14
            EMSIDEBUG  108                       Colors  15, 20
            F (FDNC)  34                         CRT environments  84
            FOLDER  108                          Custom  84
            FOLDERSCAN  108                      DESQview  122
            FORCECOMMIT  108                     DoubleDOS  123
            FORCEDPMI  108                       EGA/VGA  3, 84
            FORCEINT28  109                      M command-line parameter 
            INTL  109                                109
            L:<pwd>  109                         Margin  17
            LOGINTRO  109                        Monochrome mode  10
            M (FDSETUP)  10, 109                 NODASH  109
            M (Mailer)  12, 109                  NOISCR  110
            MSGSURVEY  109                       NOSHADOW  111
            NOCANSES  109, 117                   Program notice  62
            NOCOMMIT  109                        Screen blanking  10
            NODASH  109                          Screen flickers  9
            NODUPBCK (FDSETUP)  110              Semaphore indicators  56
            NOEKBD  110                          Show hard CRs  17
            NOEMS  110                           Timestamp in activity
            NOEMSI  110                              window  14
            NOFCB  110                           Wrap around  22
            NOFTSC1  110                     Environment variables  113
            NOICA  110                           FD  4, 5
            NOISCR  110                          FDOPT  113

                                         130




            FDOVR  113                           Available directories 
            FDSWAP  9, 113                           80
            FMOVR  113                           Event restrictions  82
            POINTNET  37, 113                    Hold (do not send)  49
            TZUTC  113                           Limiting  28, 79, 81
        Events  46, 49                           Manual (mailer)  53
            Allow file requests  49              Message status  85
            Answer inbound calls  50             Pickup  49
            BBS  48                              Protecting  82
            Behavior  47                         Request processor  83
            Days  46                             Response message  80
            Errorlevel  47                       Service requests  106
            Event manager  46                    Update request  85
            Exit when mail received              Update requests  79
                12                               XRobot  78
            External  46, 48                 Files
            File requests  82                    AUTOEXEC.BAT  4
            Forced  48                           Banner  8
            Global event (@)  46, 50             Carbon copy lists  67
            Hold (do not send) file              CONFIG.SYS  4
                attaches  49                     DOBBS.BAT  120, 121
            Inactive  48, 50                     EVENT.FD  24
            Length  47                           EXEBBS.BAT  120, 121
            Mail  46                             FD.EXE  4
            Max.cost  47                         FD.OVR  4
            Min.cost  47                         FD.SYS  5
            Modifier  46                         FDNC.EXE  4
            Overlapping  51                      FDNET.PVT  32
            Skipping forced  112                 FDNODE.CTL  30, 34, 36
            Start  47                            FDPOINT.PVT  35, 36
            Tag  46, 87, 89                      FDSETUP.EXE  4
        Fax                                      FM.EXE  4
            Editor  20                           FM.OVR  4
            Mailer  17, 42                       FOLDER.FD  24
            View from Editor  58                 Hudson Message Base  111
        FDDEV  128                               Inbound  7
        FDNODE.CTL  30                           LASTREAD.BBS  8
            COST  34                             Log  8
            DIAL  32                             MODEM.FD  111
            PHONE  32                            MSG Base  8
            POINTLIST  30, 36                    MSGHDR.BBS  8
            PVTLIST  31                          MSGIDX.BBS  8
            SWEPULSE  32                         MSGINFO.BBS  8
            Telephone number                     MSGTOIDX.BBS  8
                translation  9                   MSGTXT.BBS  8
            USE ZONE  32                         NAMES.FD  77
        FDSERVER  103                            NetMail messages  7
            %logall  104                         No BBS  8
            %nologer  104                        NODIAL.FD  56, 116
            %store  104                          NOLOCK  111
            Example  105                         Overlays  110, 113
            Limitations  104                     Packets  7
            Password  14                         PASSWORD.FD  24
            Security  106                        REQUEST.FD  24
        File requests  78                        ROUTE.FD  112, 116
            ALIAS files  80, 106                 SETUP.FD  5
            Allow  49                            Swapping  9

                                         131




        FOSSIL                                   TSRs (DOS shell)  84
            BNU  44, 122                     Messages
            Deactivating  69                     Attached files  85
            FOSSIL not loaded or                 Blind Carbon Copies  67
                detected  117                    Carbon copies  66
            Incorrect FOSSIL version             Confirmation Receipt
                117                                  Request  18
            Lock port  39                        Continuous tagging  64
            OpusComm  44                         Crash  85
            OS/2  45                             Crossposting  68
            Requirement  3                       Default status  18
            SIO/VX00  45                         Delete/sent  86
            VFD  45                              Destination  76
            X00  45, 122, 123                    Direct  86
        Handshake                                Domains  7
            DietIFNA  28, 112                    Echo info (origin lines) 
            EMSI  28, 112                            60
            EMSIDEBUG  108                       Entering  63
            FTS-1  28                            Extended information  62
            FTS-6  28                            File request  85
            LOGINTRO  109                        Folders  24
            NOEMSI  110                          Forward (manual)  57
            NOFTSC1  110                         Forwarding  90, 92
            non-FidoNet compliant                Hard CRs  17
                110                              Hold  85
            NOYOOHOO  111                        Immediate mail  48, 86
            NOZAP  112                           Import  59
            Order of priority  28                INTL  109
            Security  27                         Kill/sent  85
        Hardware                                 Lock  86
            Extended keyboard  3, 10             Margin  17
            Keypad modes  74                     No status  86
            Lock keyboard  52, 109               NOISCR  110
            Modem  38                            Origin lines  19, 25,
            NOEKBD  110                              26, 61
            NOICA  110                           Print (Editor)  61
            PC keyboards  74                     Private  85
            Raw mode (keyboard)  73              Request response  80
            Use "fastkey"  9                     Return Receipt Requests 
        Macros                                       13
            Address  77                          Sent  86
            Editor  19, 62, 65                   Status  84
            Mailer  15, 52                       Storage  7
            Terminal  23, 69, 73                 Survey  63
            UUCP  77                             Trunc/sent  85
        Mailer                                   Update requests  85
            Converting from other                UUCP  77
                124                              Zonegates  19
        Memory                               Modem  38
            EMS/XMS  3, 83, 110                  Answer control  42, 50,
            LIM/EMS  110                             54
            Minimum requirement  3               Call progress  56
            NOEMS  110                           CALLER*ID  42
            overlay  110                         CCITT V.23  39
            Scroll-back buffer  21               Command strings  40
            Swapping  16, 17, 20,                CONNECT|  40
                83, 110                          CTS/RTS  3

                                         132




            Custom message  40                   Multiple nodelists  31
            DCD forced  38                       Name lookups  76
            DCD mask  40                         Net  29
            Dialing  12, 13, 39, 41,             Node  29
                47, 49, 56                       Point  30
            Disconnect  52                       Pointlist  35
            DTE interface  3, 38                 POINTNET  37
            DTR  39                              Points  30, 35, 37
            DTR forced  38                       Region  29
            Fax  42                              Remote info  63
            FOSSIL requirement  3,               Sharing  38
                44                               Storage  8
            Hardware  38                         Zone  29
            Hiding dial info  15             Protocol  28
            Initialization  41                   Auto-Zmodem  22, 71
            Locked port  38, 39                  EMSI  96
            Maximum baudrate  39                 IEMSI  69, 71, 96
            Messages  3, 38, 40                  NORESYNC  111
            Modem manager  42, 43                NOSLO  111
            Multi-tasking  122                   SEAlink  111
            NODASH  109                          Transmit ASCII file  69
            NOMDM  111                           Zmodem  112
            ONLINE  112                      Routing  86, 112
            OS/2  45                             Allow nodes to pickup
            RING|  40                                waiting mail  49
            Send BREAK  72                       Commands  89
            Serial port  39                      comments in route file 
            SESSONDCD  112                           87
            Unable to initialize                 Debugging  112
                117                              Default rules  87
        Multi-line  113                          Dynamic  94
        Multi-tasking                            Event tag  46
            DESQview  122                        Examples  93
            DoubleDOS  123                       File routing  92
            FIFO  122                            High priority (crash)
            FILES=  4                                mail only  48
            FORCEDPMI  108                       Hold (do not send) file
            FORCEINT28  109                          attaches  49
            Hardware  122                        Host/Hub/Boss  88
            Multilink  124                       Macros  95
            NOFCB  110                           Max.cost  47
            NOMULD  111                          Min.cost  47
            NORES  111                           Multiple zones  92
            OS/2  45, 108, 122                   Nodelist flags  92, 95
            PC-MOS/386  111, 122                 Order of evaluation  94
            Semaphores  9                        points  94
            Windows  108, 122                    Scripts  97
        Nodelist                                 Send to CM systems only 
            Address browsing  76                     50
            Compiler  52                         Send to non-CM systems
            Compiling  30                            only  50
            Dial (Terminal)  72              Scripts  97
            FDNODE.CTL  36                       Commands  97
            FidoNet  5                           Labels  102
            Flags  34                            Mnemonics  103
            Hosts and hubs  30                   Node block  102
            Modem manager  43                    PC Pursuit  102, 103, 125

                                         133




        Semaphores  114
            "NE"  116
            "UD"  116
            Directory  9
            FDALIVE.n  116
            FDCANSES.n  117
            FDEXIT.nnn  116
            FDFREEZE.ALL  115
            FDFREEZE.n  115
            FDINEXIT.nnn  115
            FDINSESS.nnn  115
            FDINTERM.n  117
            FDNOEXIT.NOW  116
            FDNOSCAN.NOW  116
            FDNOUSER.NOW  116
            FDRENUM.nnn  116
            FDRESCAN.NOW  115
            FDSCAN.n  117
            FMFREEZE.n  115
            FMNEW???.n  115
            FMRESCAN.NOW  114
            Indicators  56
            MailExit  9
            New mail  18
            NODIAL.FD  116
            ROUTE.FD  116
        Service requests
            ALIAS file  106
            Parameters  107
            Service requests  106
        Support
            Help systems  124
        Technical specifications 
                128
            FDDEV  83, 107, 128
            FSC-0056  96, 110
            FTSC  128
            HMB sharing  128
            nodelist flag  95, 128
            NOLOCK  111
        Utilities
            TosScan  5, 118, 121,
                128
            XRobot  78, 124














                                         134