The CTS Serial Port Utilities (TM)

                                      User Guide






















                       Computer Telecommunication Systems, Inc





               Copyright 1993, Computer Telecommunication Systems, Inc.





          (c) Copyright 1993 Computer Telecommunication Systems, Inc. All
          Rights Reserved.

          No part of this User Guide may be reproduced, transmitted,
          transcribed, stored in a retrieval system, or translated into any
          language (natural or computer), in any form or by any means,
          without the prior written permission of Computer
          Telecommunication Systems, Inc. See the accompanying files
          VENDOR.DOC, LICENSE.DOC, and SYSOP.DOC for specific information
          pertaining to distribution of this shareware version of the User
          Guide.

          Information in this User Guide is subject to change without
          notice and does not represent a commitment on the part of
          Computer Telecommunication Systems, Inc.

          Computer Telecommunication Systems, Inc. may make improvements
          and/or changes in the User Guide and/or in Serial Port Utilities
          at any time.


          Trademarks and Copyrights

          IBM(R)  and PS/2(R)  are registered trademarks of International
          Business Machines Corporation.

          Hayes(R) is a registered trademark of Hayes Microcomputer
          Products, Inc.

          The CTS Serial Port Utilities(TM), SwapIRQ(TM), and AT Command
          Test(TM) are trademarks of Computer Telecommunication Systems,
          Inc.

          MSD is an application distributed by Microsoft Corporation 

          T/Port(TM) and Telcor(TM) are trademarks of Telcor Systems
          Corporation.

          Other names listed in this User Guide are the proprietary
          trademarks of their respective companies.


                       Computer Telecommunication Systems, Inc.
                            3847 Foxwood Road, Suite 1000
                              Duluth, Georgia USA 30136
                                 404-263-8623 (voice)
                                  404-263-0124 (fax)
                               CompuServe ID:76662,2315


                                          ii





               Copyright 1993, Computer Telecommunication Systems, Inc.






                                  TABLE OF CONTENTS

          Registration Options  . . . . . . . . . . . . . . . . . . . .  vi
               Option 1: Personal License . . . . . . . . . . . . . . .  vi
               Option 2: Personal License With Printed Documentation  .  vi
               Option 3: Professional / Corporate License . . . . . . . vii

          SPU LICENSE REGISTRATION FORM . . . . . . . . . . . . . . .  viii

          Association Of Shareware Professionals Member . . . . . . . .   x

          Acknowledgments . . . . . . . . . . . . . . . . . . . . . . .  xi

          1.0 Introducing The CTS Serial Port Utilities   . . . . . . .   1
               PORTINFO . . . . . . . . . . . . . . . . . . . . . . . .   1
               BUFFER . . . . . . . . . . . . . . . . . . . . . . . . .   2
               COM_BPS  . . . . . . . . . . . . . . . . . . . . . . . .   3
               COM_FMT  . . . . . . . . . . . . . . . . . . . . . . . .   3
               DOS_COM  . . . . . . . . . . . . . . . . . . . . . . . .   3
               DOS_SWAP . . . . . . . . . . . . . . . . . . . . . . . .   3
               DTR  . . . . . . . . . . . . . . . . . . . . . . . . . .   3
               IRQ  . . . . . . . . . . . . . . . . . . . . . . . . . .   3
               RESETCOM . . . . . . . . . . . . . . . . . . . . . . . .   3
               RTS  . . . . . . . . . . . . . . . . . . . . . . . . . .   4

          2.0 Short Instructions (Quick-Start)  . . . . . . . . . . . .   5

          3.0 The Command Line  . . . . . . . . . . . . . . . . . . . .   7
               Serial Port Number Switches  . . . . . . . . . . . . . .   8
               On / Off Switches  . . . . . . . . . . . . . . . . . . .   8
               Parameter Switches . . . . . . . . . . . . . . . . . . .   9
               Option Switches  . . . . . . . . . . . . . . . . . . . .   9

          4.0 Defining Non-Standard Serial Ports  . . . . . . . . . . .  11

          5.0 Testing Your System With PortInfo . . . . . . . . . . . .  13
               Test All Serial Ports  . . . . . . . . . . . . . . . . .  14
               Test One Serial Port . . . . . . . . . . . . . . . . . .  15
               Quick Test . . . . . . . . . . . . . . . . . . . . . . .  15
               Log File . . . . . . . . . . . . . . . . . . . . . . . .  16
               The PortInfo Summary Screen  . . . . . . . . . . . . . .  16
                    Port Configuration  . . . . . . . . . . . . . . . .  17
                         Port Address . . . . . . . . . . . . . . . . .  17
                         Interrupt (IRQ)  . . . . . . . . . . . . . . .  18
                         IRQ (Out2) Enabled . . . . . . . . . . . . . .  18
                         DOS uses port as . . . . . . . . . . . . . . .  18
                         Type of Port . . . . . . . . . . . . . . . . .  19
                         Buffer - Trigger . . . . . . . . . . . . . . .  19

                                         iii





               Copyright 1993, Computer Telecommunication Systems, Inc.





                    Port Settings . . . . . . . . . . . . . . . . . . .  20
                         Speed (BPS)  . . . . . . . . . . . . . . . . .  20
                         Bits / Character . . . . . . . . . . . . . . .  21
                         Parity . . . . . . . . . . . . . . . . . . . .  21
                         Stop Bits  . . . . . . . . . . . . . . . . . .  21
                    Hardware Signals  . . . . . . . . . . . . . . . . .  21
                         Clear to Send  . . . . . . . . . . . . . . . .  22
                         Data Set Ready . . . . . . . . . . . . . . . .  22
                         Ring Indicator . . . . . . . . . . . . . . . .  23
                         Data Carrier Detect  . . . . . . . . . . . . .  23
                         Data Terminal Ready  . . . . . . . . . . . . .  23
                         Request to Send  . . . . . . . . . . . . . . .  24

          6.0 The Other Utilities . . . . . . . . . . . . . . . . . . .  25
               BUFFER . . . . . . . . . . . . . . . . . . . . . . . . .  25
               COM_FMT  . . . . . . . . . . . . . . . . . . . . . . . .  26
               COM_BPS  . . . . . . . . . . . . . . . . . . . . . . . .  26
               DOS_COM  . . . . . . . . . . . . . . . . . . . . . . . .  27
               DOS_SWAP . . . . . . . . . . . . . . . . . . . . . . . .  27
               DTR  . . . . . . . . . . . . . . . . . . . . . . . . . .  27
               IRQ  . . . . . . . . . . . . . . . . . . . . . . . . . .  28
               RESETCOM . . . . . . . . . . . . . . . . . . . . . . . .  28
               RTS  . . . . . . . . . . . . . . . . . . . . . . . . . .  29

          7.0 PortInfo FAILURE and WARNING Messages . . . . . . . . . .  31
               Interrupt Conflicts  . . . . . . . . . . . . . . . . . .  31
                    Message PI-2010 . . . . . . . . . . . . . . . . . .  31
                    Message PI-2020 . . . . . . . . . . . . . . . . . .  32
                    Message PI-2100 . . . . . . . . . . . . . . . . . .  32
                    Message PI-2110 . . . . . . . . . . . . . . . . . .  32
                         You have multiple ports at the same address  .  33
                         You have another device using the same
                              interrupt . . . . . . . . . . . . . . . .  34
                         Your system will not let you share this
                              interrupt . . . . . . . . . . . . . . . .  34
                    Message PI-2200 . . . . . . . . . . . . . . . . . .  35
                    Message PI-2300 . . . . . . . . . . . . . . . . . .  35
               Port Conflicts . . . . . . . . . . . . . . . . . . . . .  35
                    Message PI-3000 . . . . . . . . . . . . . . . . . .  36
                    Message PI-3100 . . . . . . . . . . . . . . . . . .  36
               Mouse Conflicts  . . . . . . . . . . . . . . . . . . . .  36
                    Message PI-4000 . . . . . . . . . . . . . . . . . .  36
               DOS Port Assignments . . . . . . . . . . . . . . . . . .  37
                    Message PI-5000 . . . . . . . . . . . . . . . . . .  37
                    Message PI-5010 . . . . . . . . . . . . . . . . . .  38
                    Message PI-5020 . . . . . . . . . . . . . . . . . .  38
                    Message PI-5030 . . . . . . . . . . . . . . . . . .  38
                    Message PI-5040 . . . . . . . . . . . . . . . . . .  39
               Other CTS Software Detected  . . . . . . . . . . . . . .  39

                                          iv





               Copyright 1993, Computer Telecommunication Systems, Inc.





                    Message PI-6000 . . . . . . . . . . . . . . . . . .  39

          8.0 Customer Support Policy . . . . . . . . . . . . . . . . .  41

          9.0 About Computer Telecommunication Systems  . . . . . . . .  43
               AT Command Test  . . . . . . . . . . . . . . . . . . . .  43
               SwapIRQ  . . . . . . . . . . . . . . . . . . . . . . . .  43
               MouseOFF and MouseON . . . . . . . . . . . . . . . . . .  43
               Serial Cards (Comm Ports)  . . . . . . . . . . . . . . .  44
               Modems . . . . . . . . . . . . . . . . . . . . . . . . .  44
               Fax / Modem / Phone Switches . . . . . . . . . . . . . .  44
               Surge Protection Devices . . . . . . . . . . . . . . . .  44
               Cables / Adapters  . . . . . . . . . . . . . . . . . . .  44
               Custom Programming Services  . . . . . . . . . . . . . .  44
               New Products . . . . . . . . . . . . . . . . . . . . . .  44



































                                          v





               Copyright 1993, Computer Telecommunication Systems, Inc.





          Registration Options
          ====================
          Three different registration options are available: 

          Option 1: Personal License
          --------------------------
          This is the most economical registration for a personal user. If
          you need to use the SPU to diagnose a problem with your personal
          computer, then this is the license for you. By registering, you
          obtain personalized support to assist you with trouble-shooting
          your computer. Details are provided in the User Guide section
          titled "Customer Support Policy". As part of this license, you
          also receive: 

            *  30 minutes of personal assistance with your serial port
               problems.

            *  The most current version of the Serial Port Utilities.

            *  FREE minor version updates.

            *  Announcements about major updates. You will receive a FREE
               upgrade to any major update within 6 months of your
               registration.

          The license provided with this option allows the registered user
          to use the SPU on any computer personally owned by the registered
          user. 

          Option 2: Personal License With Printed Documentation
          -----------------------------------------------------
          This registration option provides all of the benefits of the
          Personal License (Option 1), and also includes the following:

            *  60 minutes of personal assistance with your serial port
               problems.

            *  A printed copy of the User Guide.

            *  Announcements about major updates. You will receive a FREE
               upgrade to any major update within 12 months of your
               registration.

            *  Supplemental technical information discussing serial port
               basics, types of serial ports, when and why you need a
               16550A UART, how and when you can share interrupts between
               serial ports, details of the RS-232 interface, cable wiring,
               and how IRQ 2 and IRQ 9 are used.


                                          vi





               Copyright 1993, Computer Telecommunication Systems, Inc.





            *  The MouseOn and MouseOff utilities. The "mouse utilities"
               allow a mouse and a modem to share the same interrupt when
               running under DOS.

            *  The first 250 registrants (options 2 and 3 only) will
               receive a free copy of SwapIRQ. SwapIRQ is a DOS utility
               which allows communications applications to use a serial
               port on any IRQ. 

          The license provided with this option allows the registered user
          to use the SPU on any computer personally owned by the registered
          user.


          Option 3: Professional / Corporate License
          ------------------------------------------
          This license is for consultants and corporate support specialists
          who routinely deal with a multiple computers. Treat the SPU like
          your screwdriver - that is, as long as it is in your possession
          and not left at any other machine, you are in compliance with the
          license. Only one individual is authorized to call for support.

          This license option provides the same benefits as Option 2, but
          includes expanded technical support (90 minutes) and a license
          which allows use of the SPU on multiple computers as long as the
          SPU is only installed on one computer at a time. 

          Site licenses are available for situations where multiple
          installed copies are required.





















                                         vii



                            SPU LICENSE REGISTRATION FORM

          Name: _________________________________________________________

          Daytime telephone: __________________  Evening: _______________

          Fax Number: _________________    CompuServe ID: _______________

          Company Name: _________________________________________________

          Address: ______________________________________________________

                   ______________________________________________________

            ALL ORDERS - Choose format: 5.25" ____ 3.5" ____

          QTY   Description                      Unit Price      Subtotal
          ===   ===========                      ==========      ========
          ___   Option 1: Personal License           $20.00     $________

          ___   Option 2: Personal License With 
                     Printed Documentation           $30.00     $________

          ___   Option 3: Professional /
                      Corporate License              $50.00     $________

          Sales Tax:               Georgia residents add 5%     $________

          Shipping / Handling:
               Option 1: USA..........................$2.00
                         All other countries .........$4.00

               Options 2&3: USA/Canada/Mexico ....... $4.00
                          All other countries ....... $8.00     $________

                                   TOTAL (US dollars, please)   $________

          PAYMENT METHOD:    Cash __           Check__      Money Order__
                             Visa __      MasterCard__         Discover__

          =================================================================
                               CREDIT CARD INFORMATION
          =================================================================

          Name as it appears on the card: _________________________________

          Card No. ________  ________  ________  ________  Expires  ___/___

          Cardholder signature: ___________________________________________

          =================================================================
                                       SEND TO
          =================================================================
                       Computer Telecommunication Systems, Inc.
                            3847 Foxwood Road, Suite 1000
                              Duluth, Georgia USA 30136
                                 404-263-8623 (Voice)
                                  404-263-0124 (FAX)
                                CompuServe: 76662,2315

                 NOTE: Prices are subject to change without notice. 





               Copyright 1993, Computer Telecommunication Systems, Inc.





                                DISCLAIMER OF WARRANTY

          USERS OF THIS SOFTWARE MUST ACCEPT THIS DISCLAIMER OF WARRANTY:

          THIS SOFTWARE IS SUPPLIED AS IS. COMPUTER TELECOMMUNICATION
          SYSTEMS DISCLAIMS ALL WARRANTIES, EITHER EXPRESS OR IMPLIED,
          INCLUDING BUT NOT LIMITED TO IMPLIED WARRANTIES OF
          MERCHANTABILITY AND FITNESS FOR A PARTICULAR PURPOSE, WITH
          RESPECT TO THE SOFTWARE AND THE ACCOMPANYING WRITTEN MATERIALS. 

          NO LIABILITY FOR CONSEQUENTIAL DAMAGES. IN NO EVENT SHALL
          COMPUTER TELECOMMUNICATION SYSTEMS OR ITS SUPPLIERS BE LIABLE FOR
          ANY DAMAGES WHATSOEVER (INCLUDING, WITHOUT LIMITATION, DAMAGES
          FOR LOSS OF BUSINESS PROFITS, BUSINESS INTERRUPTION, LOSS OF
          BUSINESS INFORMATION, OR OTHER PECUNIARY LOSS) ARISING OUT OF THE
          USE OF OR INABILITY TO USE THIS COMPUTER TELECOMMUNICATION
          SYSTEMS PRODUCT, EVEN IF COMPUTER TELECOMMUNICATION SYSTEMS HAS
          BEEN ADVISED OF THE POSSIBILITY OF SUCH DAMAGES. BECAUSE SOME
          STATES DO NOT ALLOW THE EXCLUSION OR LIMITATION OF LIABILITY FOR
          CONSEQUENTIAL OR INCIDENTAL DAMAGES, THE ABOVE LIMITATION MAY NOT
          APPLY TO YOU.





























                                          ix





               Copyright 1993, Computer Telecommunication Systems, Inc.







          Association Of Shareware Professionals Member
          =============================================


                        _______
                   ____|__     |                (R)
                --|       |    |-------------------
                  |   ____|__  |  Association of
                  |  |       |_|  Shareware
                  |__|   o   |    Professionals
                -----|   |   |---------------------
                     |___|___|    MEMBER


          This program is produced by a member of the Association of
          Shareware Professionals (ASP). ASP wants to make sure that the
          shareware principle works for you. If you are unable to resolve a
          shareware-related problem with an ASP member by contacting the
          member directly, ASP may be able to help. The ASP Ombudsman can
          help you resolve a dispute or problem with an ASP member, but
          does not provide technical support for members' products.  Please
          write to the ASP Ombudsman at 545 Grover Road, Muskegon, MI
          49442-9427 USA, FAX 616-788-2765 or send a CompuServe message via
          CompuServe Mail to ASP Ombudsman 70007,3536.
























                                          x





               Copyright 1993, Computer Telecommunication Systems, Inc.





          Acknowledgments

          I wish to express my very special thanks to the following
          individuals who made this application possible. The CTS Serial
          Port Utilities would not exist today without their suggestions,
          assistance, and, most importantly, the time they invested in
          testing the thirty or so iterations of the SPU during the six
          month BETA test program. 

               David Bittner, who received, tested, and reported back on
               more iterations of the SPU than I had a right to expect of
               anyone! 

               Dan Landiss, who identified an internal modem which the SPU
               didn't like...and hung in there running tests until I got it
               right!

               Earle Robinson, who really has the knack for product
               testing. He broke some of the early versions of the SPU more
               often and faster than anyone!

               And, finally, Tom Wason, who wrote a six page letter filled
               with suggestions and comments. I had to agree with
               everything he said! Tom...if you mentioned it, it's here!

          In addition, there were individuals too numerous to list who
          tested at least one version of the SPU and reported back
          suggestions or verified that known problems were fixed. To each
          of you, my thanks!





















                                          xi





               Copyright 1993, Computer Telecommunication Systems, Inc.





          1.0 Introducing The CTS Serial Port Utilities 

          Serial ports (also known as comm ports) are painless when they
          work, and a pain in the neck when they don't. They have plenty of
          options and limitations. They need a unique address, an inactive
          IRQ, and software which is properly configured to use it. No
          wonder nearly everyone gets confused by serial ports.

          The CTS Serial Port Utilities (SPU) is a collection of DOS
          software utilities that provide you with control over the serial
          ports in your computer. Most serial port problems can be resolved
          by using these utilities. Each of the utilities support all
          standard and any user-defined serial ports. User-defined ports
          are defined in the command line or in your system environment
          variables.

          Why "Oh, NO! NOT ANOTHER?" serial port utility? Well, several
          good reasons come to mind. The first is that there were a lot of
          things still not done by other utilities. Can you name one which
          detects multiple serial ports installed at the same address
          (other than the SPU?) Or one that tells you when your monitor
          will cause problems if you use COM4? Want to know what the
          current receiver trigger level is in your 16550A serial port?
          Better use the SPU program PortInfo to find out! Nothing else out
          there today will tell you! The SPU even detects the T/Port 
          serial card, and identifies some internal modems that have
          "emulated UARTs".

          More reasons? We spent a lot of time reviewing the utilities that
          were out before SPU, and didn't find one that was both good and
          full-featured. There were a few that were very good for limited
          applications, but didn't properly test IRQ assignments, or were
          limited in the serial ports they supported, or....well, you get
          the idea. It just seemed like it was time for a common set of
          utilities that tied everything together.

          So the CTS Serial Port Utilities came into being. The utilities
          all share a common command line interface, and they all use a
          common set of environment variables you can set to define non-
          standard serial ports. The SPU contains the following programs:


               1.1 PORTINFO

               PortInfo is a comprehensive utility which tests your system
               to determine everything possible about your serial ports,
               including interrupt and address conflicts. PortInfo provides
               you with FAILURE and WARNING messages about actual and
               possible conflicts. 

                                          1





               Copyright 1993, Computer Telecommunication Systems, Inc.





               PortInfo provides details on the following:
                *   Multiple serial ports at the same address (eg, 2 Com1
                    ports)
                *   Interrupt conflicts between a bus mouse and a serial
                    port
                *   Shared interrupts (2 serial ports, or a serial port and
                    a serial mouse sharing an IRQ)
                *   Conflicts COM4 and 8514/A compatible monitors
                *   Unusual default serial port setups (BIOS and DOS port
                    assignments)
                *   Serial ports that cannot generate interrupts
                *   Helps to determine when interrupts can be shared

               Other information provided:
                *   Actual IRQ used by each port and the current IRQ status
                *   DOS port assignments (com1-com4, mouse)
                *   Port (UART) Identification (8250, 8250A/16450, 16550,
                    16550A, the T/Port, and some "emulated UARTs"
                *   FIFO status: If it exists, on / off, else 'None'
                *   If the FIFO is ON, the current FIFO receiver trigger
                    level is displayed.
                *   All programmable port parameters: speed, format,
                    parity, current RTS and DTR settings
                *   Current status of modem lines: Ring Indicator, Carrier
                    Detect, Clear to Send, Data Set Ready, with indication
                    of when the lines are tied together (looped back).

               Other features:
                *   Ports are COMPLETELY restored to their original
                    settings
                *   Supports standard serial ports 1-4 on PC/AT, 1-8 on
                    PS/2
                *   Supports up to 8 user definable (port address and IRQ)
                    serial ports
                *   Displays detailed messages about conflicts with
                    reference numbers to assist looking up the detailed
                    assistance in the section titled "PortInfo FAILURE and
                    WARNING Messages". 


               1.2 BUFFER

               Buffer allows you to control the FIFO buffers in a 16550A or
               compatible UART. You can turn the buffers on and off, and
               set the receiver trigger level. See the section titled
               "Testing Your Software with PortInfo...Buffer-Trigger" for
               more information on UART FIFO receiver trigger levels.



                                          2





               Copyright 1993, Computer Telecommunication Systems, Inc.





               1.3 COM_BPS

               COM_BPS allows you to set a port data rate (in bits per
               second, or BPS) to any standard value supported by the
               serial port. This utility is normally used as a replacement
               for the DOS set mode command. 


               1.4 COM_FMT

               COM_FMT allows you to set a port character format to any
               standard value supported by the serial port. This utility is
               normally used with COM_BPS as a replacement for the DOS mode
               command. 


               1.5 DOS_COM

               You can use DOS_COM to insert a serial port in the list of
               ports used by DOS.


               1.6 DOS_SWAP

               You can use DOS_SWAP to exchange two serial ports in the
               list of ports used by DOS.


               1.7 DTR

               DTR gives you command line control of the Data Terminal
               Ready (DTR) line of any serial port. 


               1.8 IRQ

               IRQ allows you to enable and disable the interrupts from any
               serial port.


               1.9 RESETCOM

               ResetCom resets a port to a "power-up" configuration: Port
               interrupts are disabled, data rate is set to 2400 bps,
               character format to eight data bits, no parity, one stop
               bit. If the port is a 16550A family device, then the buffers
               (FIFOs) are disabled. This utility will often restore a port
               that doesn't work after running an ill-behaved application.


                                          3





               Copyright 1993, Computer Telecommunication Systems, Inc.





               1.10 RTS

               RTS gives you command line control of the Request to Send
               (RTS) line of any serial port. 














































                                          4





               Copyright 1993, Computer Telecommunication Systems, Inc.





          2.0 Short Instructions (Quick-Start)

          Each of the utilities provides a short help screen when you enter
          the program name followed immediately by the return key. This
          help screen includes a brief description of what each utility
          does and the valid command line switches used to control it. For
          example, if you wanted to see the help screen for PortInfo, you
          would enter:

                    PortInfo <Enter>

               After reading the help screen, you might decide to do the
               basic system test with the command:

                    PortInfo /0 <Enter>

               NOTE: This only works for standard serial port addresses.
               Refer to the following documentation for information on how
               to test serial ports located at any address.


          We've occasionally observed situations with internal modems that
          require the computer to have a hard reset before running PortInfo
          to obtain correct results. If you observe a problem where
          PortInfo does not detect an internal modem or the IRQ used by the
          modem, then either turn your computer off and back on to perform
          a hard reset, or, if your computer has a RESET button, press it.
          Then try running PortInfo again.

          NOTE: a soft reset (control-alt-delete) is not sufficient to
          reset these modems to a state where PortInfo can recognize them.
          You must do a "hard reset" as described above.


















                                          5





               Copyright 1993, Computer Telecommunication Systems, Inc.























































                                          6





               Copyright 1993, Computer Telecommunication Systems, Inc.





          3.0 The Command Line

          The Serial Port Utilities are controlled by "command line
          switches" that you enter on the command line. Command line
          switches are program options that you place on the command line.
          Each option is preceded by a slash character "/". These
          "switches" control the SPU software the way a hardware switch
          controls the options on a board.

          The standard command line format is:

               Program_Name /switch1 /switch2 ... <Enter>

          For each of the utilities, you can enter either the program name
          by itself or with a "/? command line switch" to display a brief
          description of the utility and the switches used to control it.
          For example, both of the following commands will display the help
          screen for PortInfo:

               PortInfo /? <Enter>

               or

               PortInfo <Enter>

          where <Enter> means you should press the Enter or Return key.

          There are some general rules for the command line switches:

          1. You may enter the command line switches in any order UNLESS a
          fixed sequence is defined for a particular utility. 

          2. You can enter the command line switches as uppercase or
          lowercase letters.

          3. You may optionally leave one space between different values in
          a single command line switch.

          To demonstrate, the following commands all do the same thing (it
          sets the data rate to 9600 bps for COM1):

               COM_BPS /1 /S9600 <Enter>
               com_BPS /s 9600 /1 <Enter>
               com_bps /1 /S 9600 <Enter>
               com_bps /1/s9600 <Enter>
               CoM_BpS/1/s9600 <Enter> 




                                          7





               Copyright 1993, Computer Telecommunication Systems, Inc.





          Choose a format to use that is comfortable for you. You will
          receive a format error message if you enter a string the utility
          doesn't understand.

          There are four formats of switches in addition to the help
          switch:


               3.1 Serial Port Number Switches

               Each of the utilities can work on a defined serial port
               specified as a number, or on all serial ports that are
               standard of defined for the CTS Serial Port Utilities (see
               the next chapter for instructions on how to define a non-
               standard port.)

               The command line switch for port assignments is simply a "/"
               (the switch command) followed by the port number. For
               example, to run PortInfo on serial port one, you would
               enter:

                    PortInfo /1 <Enter>

               Specifying serial port zero (a non-existent port) will cause
               the utility, to operate on all of the serial ports. For
               example, to run PortInfo on all standard and user-defined
               serial ports, you would enter the command:

                    PortInfo /0 <Enter>


               3.2 On / Off Switches

               Some utilities control a serial port function that is turned
               on or off. For example, to turn "On" the DTR line for serial
               port 2, you enter:

                    DTR /on /2 <Enter>       -OR-
                    DTR /ON /2 <Enter>       -OR-
                    DTR /2 /On <Enter>

                    Remember, they all do the same thing!

               To turn a function off, you use the "/Off" switch rather
               than "/On".





                                          8





               Copyright 1993, Computer Telecommunication Systems, Inc.





               3.3 Parameter Switches

               There are a number of these switches which you use to enter
               a value. One example was shown above when we set the port
               data rate to 9600 bps with the "/Sspeed" parameter switch.
               Parameter switches are also used to define a non-standard
               serial port, to set port formats, receive trigger levels for
               a 16550A fifo, and to define a particular interrupt (IRQ) to
               use. Check the help screen for each utility to see which
               parameter switches are used.


               3.4 Option Switches

               These are two option switches used in PortInfo to control
               how it operates. The switch "/Q" instructs PortInfo to do a
               quick test, and "/L" causes a file named "PORTINFO.LOG" to
               be created containing an copy of all messages displayed to
               the screen. See the Section "Testing Your System With
               PortInfo" for details.






























                                          9





               Copyright 1993, Computer Telecommunication Systems, Inc.





          

















































                                          10





               Copyright 1993, Computer Telecommunication Systems, Inc.





          4.0 Defining Non-Standard Serial Ports

          The CTS Serial Port Utilities will work with any serial port on
          any interrupt (IRQ). However, if you have serial ports other than
          the standard COM1-COM4, then you have to tell the SPU where the
          ports are (that is, what address the port is installed on.) You
          have two different ways to do this: 

          1. you can run each of the utilities using the serial port
          address switch "/Aaaa", where "aaa" is the first address location
          (the "base address") used by the serial port

          2. you can define a system environment variable for each non-
          standard serial port that will make the ports available to the
          SPU via port numbers. 

          The CTS SPU recognizes an environment variable with the following
          format:

               CTSCOMn= /Aaaa

          where:
               "n" is the serial port number you are assigning to the Com
               port 
               "aaa" is the first address location (the "base address") for
               the serial port

          NOTE: Make sure there is NO space between the com port number and
          the "="

          You define an environment variable with the DOS "SET" command,
          which you can enter at the DOS command line or place into a batch
          file (such as your AUTOEXEC.BAT file.) You DOS manual provides
          documentation on the SET command.

          Examples: 

          1. Define a port at base address 1E0 (hexadecimal) as COM5:

               CTSCOM5= /A1E0










                                          11





               Copyright 1993, Computer Telecommunication Systems, Inc.





          2. Define a port at base address 2E0 as COM6:

               CTSCOM6= /a 2E0

          Using these two examples, you may now access the two non-standard
          serial ports as COM5 and COM6 in all utilities of the SPU. These
          serial ports will also be used by any utility that is used with
          the "/0" (all ports) command line.

          NOTE: The CTSCOMn environment variables are not used by any other
          applications except SwapIRQ, another CTS product which allows DOS
          software to use any IRQ. 






































                                          12





               Copyright 1993, Computer Telecommunication Systems, Inc.





          5.0 Testing Your System With PortInfo

          The first thing to do after installing the Serial Port Utilities
          is to run PortInfo to do a full system test. If you have a mouse,
          make sure that your mouse driver is loaded. PortInfo will
          discover many common problems with your serial ports, including: 

            *  multiple ports installed at the same address
            *  interrupt conflicts with other devices
            *  conflicts between your mouse and serial ports
            *  identifies which serial ports are sharing an interrupt
            *  identifies serial ports which are not able to generate an
               interrupt
            *  possible problems with the DOS definitions for the serial
               ports
            *  Identifies some displays which conflict with the standard
               COM4 serial port

          PortInfo will only run from DOS, not from a DOS session within
          Windows or OS/2, or under DesqView. These operating environments
          prevent the PortInfo utility from directly testing the serial
          ports. If you are running Windows, you will need to exit to DOS
          before running PortInfo. If you are running OS/2, you will need
          to re-boot your system to run DOS before starting PortInfo.

          The summary screen provides information about the type of UART
          used in the serial port  and the current settings for the port.
          You want to pay particular attention to the FAILURE and WARNING
          messages that appear the first time you run PortInfo. All
          messages and the summary screen can be captured to a "log file"
          for later use or reference.

          PortInfo reports a FAILURE message when there is a problem
          detected with your system that will prevent correct operation.
          Failures are typically reported for conflicts between a serial
          port and another serial port or device. 

          A WARNING message is reported by PortInfo when there is no
          immediate problem that you have to fix, but there is a situation
          that could lead to a problem if you are not careful. For example,
          if you have two different serial ports using the same interrupt,
          a WARNING will be reported. If you are careful, you can usually
          share the IRQ between the ports - BUT the potential for a problem
          exists.

          Both warning and failure messages have a message number. Save the
          message number(s) for reference to the section titled "PortInfo
          FAILURE and WARNING Messages". You will find each message


                                          13





               Copyright 1993, Computer Telecommunication Systems, Inc.





          explained in more detail with a description of the most common
          solutions for the problem.

          We've occasionally observed situations with internal modems that
          require the computer to have a hard reset before running PortInfo
          to obtain correct results. If you observe a problem where
          PortInfo does not detect an internal modem or the IRQ used by the
          modem, then either turn your computer off and back on to perform
          a hard reset, or, if your computer has a RESET button, press it.
          Then try running PortInfo again.

          NOTE: a soft reset (control-alt-delete) is not sufficient to
          reset these modems to a state where PortInfo can recognize them.
          You must do a "hard reset" as described above.

               5.1 Test All Serial Ports

               To start PortInfo to do a complete test of all ports, enter
               the following command:

                    C:> PortInfo /0 <Enter>

               This tells PortInfo to do a full test of all standard serial
               ports (remember, /0 is the command for all ports), and all
               non-standard serial ports you have defined using the CTSCOMn
               environment variables for the CTS Serial port Utilities. 

               NOTE: If you have a non-standard serial port installed, it
               will not be tested unless you have defined a CTSCOMn
               environment variable.




















                                          14





               Copyright 1993, Computer Telecommunication Systems, Inc.





               5.2 Test One Serial Port

               You can also have PortInfo test only a single serial port.
               You can tell PortInfo to test a single serial port in two
               different ways. One way is to specify the serial port number
               you want to test. For example, the following command will
               test COM2:

                    C:> PortInfo /2 <Enter>

               You can also test a serial port by specifying the serial
               port address. This is the only way you can test a non-
               standard serial port without a CTSCOMn environment variable.
               For example, if you want to test the port at address 01E0
               (hex), you would enter:

                    C:> PortInfo /A 1E0 <Enter>


               5.3 Quick Test

               You may tell PortInfo to do a "quick test" if you are in a
               hurry to just check out a port setting. The quick test skips
               most of the conflict tests, so it will generally not detect
               port conflicts. You can specify the quick test for both a
               single port test and the complete system test. To specify
               the quick test, add a "/Q" (for Quick) to the command line
               as shown below:

               Example 1: Do a quick test on all ports:

                    C:> PortInfo /0 /Q <Enter>

               Example 2: Do a quick test on COM3:

                    C:> PortInfo /3 /Q <Enter>














                                          15





               Copyright 1993, Computer Telecommunication Systems, Inc.





               5.4 Log File

               PortInfo can create a copy of all messages and the summary
               screen on your disk that you can use to refer to when
               installing new equipment in your computer. When you use the
               "/L" command line switch, PortInfo creates a file named
               "PORTINFO.LOG" in your default directory. This file contains
               all information that is displayed on the screen while
               PortInfo runs.

               Example: Do a full system test, and save the results in the
               "PORTINFO.LOG" file:

                    C:> PortInfo /0 /L <Enter>


               5.5 The PortInfo Summary Screen

               PortInfo completes operation by displaying a summary of all
               information it gathered while testing. The following is a
               sample display for a system with four or less serial ports
               (eight columns are displayed for more serial ports.) Each
               item on the display is discussed in the following sections. 



                               PortInfo Summary Screen























                                          16





               Copyright 1993, Computer Telecommunication Systems, Inc.





                                   Serial 1   Serial 2  Serial 3  Serial 4

           Port Address (Hex)           3F8        2F8       3E8       N/A
           Interrupt (IRQ)                4          3        10
           IRQ (Out2) Enabled            No        Yes        No

           DOS uses port as            Com1      Mouse      Com3       N/A
           Type of Port              T/Port      16450    16550A   Display
           Buffer - Trigger            None       None      On-8

           Speed                      19200       1200      2400
           Bits / Character               8          7         8
           Parity                      None       None      None
           Stop Bits                      1          1         1

           Clear to Send                 On        Off       Off
           Data Set Ready                On        Off       Off
           Ring Indicator               Off        Off       Off
           Data Carrier Detect           On        Off       Off
           Data Terminal Ready          Off         On       Off
           Request to Send              Off         On       Off


                    5.5.1 Port Configuration


                         5.5.1.1 Port Address

                         This line shows the "base port address" in
                         hexadecimal for each serial port detected. The
                         "base port address" is the first address used by
                         the serial port. Serial ports normally use eight
                         address locations, so the term "base port address"
                         is used to refer to the first address used. In the
                         example displayed above, the COM1 base port
                         address is 03F8 (hex). The serial port actually
                         uses eight consecutive addresses starting at 03F8
                         and ending at 03FF (hex).












                                          17





               Copyright 1993, Computer Telecommunication Systems, Inc.





                         5.5.1.2 Interrupt (IRQ)

                         The Interrupt (IRQ) line of the display shows the
                         actual hardware interrupt used by the serial port.
                         This value is determined by testing the serial
                         port. If a NOTE is displayed in this field, then
                         there is a possible conflict with this port that
                         will cause a problem if you try to use the port. 


                         5.5.1.3 IRQ (Out2) Enabled

                         This line shows the current status of the OUT2
                         line for the serial port. The OUT2 line is a UART
                         control line used by some communication software
                         to enable the IRQ. A serial port cannot generate
                         interrupts when this line is disabled, OR when
                         another serial port that uses the same IRQ line is
                         enabled. 

                         If you have two serial ports sharing an IRQ with
                         an "Enabled" status, or if you have a problem
                         using one port when the other shows an "Enabled"
                         status, then you need to disable the OUT2 line on
                         the inactive port. You can do this with two
                         different utilities provided in the SPU.
                         "ResetCom" will restore a serial port to it's
                         original power-up status, and "IRQ" provides you
                         with direct control of the IRQ (Out2) line. These
                         utilities are described below.


                         5.5.1.4 DOS uses port as

                         This line will show how DOS expects to use this
                         port. If a mouse is detected, the word "Mouse"
                         will be displayed as shown for above for Serial 2.
                         Otherwise, the field will contain the DOS default
                         port assignments as detected by your system bios
                         at boot-up time. If the letters "N/A" are
                         displayed, then the port is Not Available for use
                         by commands like the DOS Mode command. You can
                         adjust these port assignments with the DOS_COM and
                         DOS_SWAP utilities provided with PortInfo. 






                                          18





               Copyright 1993, Computer Telecommunication Systems, Inc.





                         5.5.1.5 Type of Port

                         The Type of Port line describes the type of UART
                         detected by PortInfo. If no UART was detected for
                         the port, the letters "N/A" will be displayed.
                         Also notice that the word "Display" appears on the
                         COM4 port. There are some display cards, including
                         the Diamond Stealth, the ATI Ultra Graphics, and
                         others which emulate IBM 8514/A displays that use
                         the address space normally reserved for COM4.
                         PortInfo detects the presence of many of these
                         displays and identifies the port as such.

                         NOTE: that there are two types of UARTs which
                         software cannot tell apart: the 8250A and the
                         16450. PortInfo chooses to display this UART type
                         as a "16450" since the 16450 is the most common
                         UART used today. Other diagnostic software may
                         identify the UART as an 8250A (or even an 8250,
                         which is incorrect). 


                         5.5.1.6 Buffer - Trigger

                         One of the unique features of PortInfo is it's
                         ability to sense not only the status of the FIFO
                         buffer on a 16550A, but also to detect what
                         receiver trigger level is being used. This line
                         will display "None" for those UARTs that do not
                         have buffers, Off for 16550A compatible UARTs
                         whose buffers are not enabled, and On-#, where #
                         will be 1, 4, 8, or 14 to show that the FIFO
                         buffer receiver trigger is set to.

                         The receiver trigger level for a 16550A UART
                         determines when it will issue an interrupt
                         request. If the trigger is set to 14, the UART
                         will issue the interrupt after 14 of the 16 spots
                         in the buffer are filled. This reduces the number
                         of interrupts generated by the UART, but only
                         leaves three character times for the PC to service
                         the interrupt before data is lost. Reducing the
                         trigger level to 8 increases the number of
                         interrupts (1 interrupt for every 8 characters
                         received), but greatly reduces the possibility of
                         data loss since the PC has 9 character periods
                         before an overrun will occur. If you experience
                         data loss at high speed in a communication
                         program, try exiting to DOS while connected and

                                          19





               Copyright 1993, Computer Telecommunication Systems, Inc.





                         run PortInfo on the port. If the Buffer - Trigger
                         shows "Off", then your software may not support
                         the 16550A UART. You can try enabling the buffer
                         with the trigger set to one (1) with the "Buffer"
                         utility and then exit to your communication
                         software. This change may cause your communication
                         software to lock up, however. If so, your only
                         recourse is to contact the software manufacturer
                         for an update, or change to another communications
                         application.

                         If PortInfo displays "On-14", try using the
                         "Buffer" utility to reset the trigger level to
                         eight (8). This should reduce or eliminate the
                         overrun problem. Making this change should not
                         adversely affect your communications software, but
                         may eliminate your overrun problems.


                    5.5.2 Port Settings

                    The following port settings are normally controlled by
                    your communication software.


                         5.5.2.1 Speed (BPS)

                         This line shows the current port data rate in bits
                         per second (BPS). You normally control this value
                         in your communication program, but you can change
                         this value with the DOS Mode command, or with the
                         COM_BPS utility provided with PortInfo. The
                         advantage of the COM_BPS utility is that it allows
                         setting data rates up to 115,200 bps, and supports
                         ports not recognized by DOS. 

                         NOTE: to convert to characters per second, you
                         normally divide the BPS value by 10. That is, a
                         serial port sending characters at 19,200 bps is
                         sending 1,920 characters (or bytes) per second.










                                          20





               Copyright 1993, Computer Telecommunication Systems, Inc.





                         5.5.2.2 Bits / Character

                         The bits per character line displays the number of
                         data bits used for each character. Allowable
                         values are 5, 6, 7, and 8. You can control the
                         bits per character with the COM_FMT utility
                         provided with PortInfo. This setting is normally
                         controlled by your communications software, but is
                         provided here for control of non-standard ports
                         not supported by the DOS Mode command.


                         5.5.2.3 Parity

                         The Parity line shows the current parity bit
                         setting for the port. The possible values are
                         None, Even, Odd, Mark, and Space. You can control
                         the port format with the COM_FMT utility provided
                         with PortInfo.


                         5.5.2.4 Stop Bits

                         This line shows the number of stop bits sent with
                         each character. Valid values for the number of
                         stop bits are 1, 1.5, and 2. You can control the
                         number of stop bits with the COM_FMT utility
                         provided with PortInfo.


                    5.5.3 Hardware Signals

                    The serial port hardware signals are used by different
                    modems and devices in different ways. The RTS line is
                    often used for hardware flow control, or it may be used
                    to provide power to a portable modem. It's also
                    possible for a cable, connector, or a serial port board
                    to provide a means of looping back, or connecting lines
                    to each other. If you see a hardware line listed as "On
                    - DTR" or "Off - RTS", then this means that the line
                    indicated is in the state shown, and it *may* be
                    connected to the line indicated. These results can be
                    affected by the devices connected to the serial port.
                    You can disconnect the device and cables to determine
                    where the loopback condition occurs. 

                    Common uses for each line are discussed below. 



                                          21





               Copyright 1993, Computer Telecommunication Systems, Inc.





                         5.5.3.1 Clear to Send

                         The Clear To Send (CTS) line is commonly used by
                         modems and other devices for "hardware flow
                         control". Flow control is used to prevent data
                         from being sent faster than it can be processed.
                         The CTS line is input only - it is controlled by
                         the device attached to your serial port. Your
                         modem can use the CTS line to start and stop the
                         flow of data sent by your computer when your
                         software supports hardware flow control.

                         The CTS line is normally "Off" when the serial
                         port has nothing connected to it, or if it is
                         connected to a device like a serial mouse or a
                         scanner. When your serial port is connected to a
                         Hayes compatible modem, and the modem is turned
                         on, CTS should be "On" at all times except when
                         the modem is connected to a remote system, and the
                         modem has signalled the software to stop sending
                         information. If you detect that CTS is not "On"
                         for your modem when there is no connection, then
                         you may have one of the following conditions: 1)
                         Your cable between the serial port and the modem
                         does not contain the CTS line. This means you will
                         NOT be able to use hardware flow control with your
                         modem; 2) Your modem is not a true Hayes-
                         compatible modem; 3) Your modem is not operating
                         correctly; or 4) Your serial port is not working
                         correctly. 


                         5.5.3.2 Data Set Ready

                         The Data Set Ready (DSR) is a line which
                         historically is used by modems (data sets) to
                         signal when they are connected to a remote modem
                         and ready to send data. This line is input only -
                         it is controlled by the device attached to your
                         serial port.

                         Most modems today allow you to configure how this
                         line is used. The default for Hayes and compatible
                         modems is to turn this line "On" when the modem is
                         powered on. On some modems, you can also configure
                         this line to be "Off" at all times except when
                         connected with a remote modem.



                                          22





               Copyright 1993, Computer Telecommunication Systems, Inc.





                         5.5.3.3 Ring Indicator

                         The ring indicator line is normally used by modems
                         to signal that a ring was detected on the phone
                         line. This line is input only - it is controlled
                         by the device attached to your serial port.

                         PortInfo will normally detect this line as "Off"
                         with a modem unless you manage to get a ringing
                         signal at the exact moment PortInfo checks the
                         status of the line. 


                         5.5.3.4 Data Carrier Detect

                         The Data Carrier Detect (DCD) line is normally
                         used by a modem to signal that the modem is
                         connected to a remote modem and ready to exchange
                         information. This line is input only - it is
                         controlled by the device attached to your serial
                         port.

                         Many modems can be configured so that DCD is "On"
                         all of the time with a command (the &C command is
                         used by Hayes and true compatible modems) or with
                         a switch on the modem.


                         5.5.3.5 Data Terminal Ready

                         The Data Terminal Ready (DTR) line is a line
                         output by the serial port to the connected device.
                         Historically, the DTR line was used by old "dumb
                         terminals" to signal the modem that they were
                         ready to receive data. 

                         The DTR line typically has two different uses
                         today with modems. Most common is to use the DTR
                         line to end a connection. Your modem can look for
                         a signal from your communication software to force
                         a hangup. In some cases, this will also hang up
                         the modem.

                         The second use for this line is to provide power
                         to the "line powered" portable modems introduced
                         over the last couple of years. Some portable
                         modems have no power supply or batteries, and
                         actually use the telephone line, the DTR line, and
                         the RTS line (see below) to supply their power. If

                                          23





               Copyright 1993, Computer Telecommunication Systems, Inc.





                         you have one of these modems, then make sure that
                         DTR is high if you try to use the modem. Most
                         communication software does this automatically,
                         but some utilities that send modem commands from
                         the DOS prompt may not. You can use the "DTR"
                         utility that comes with PortInfo to control the
                         DTR line.


                         5.5.3.6 Request to Send

                         The Request to Send (RTS) line is another line
                         output by the serial port to the connected device.
                         This line typically is used for hardware (RTS/CTS)
                         flow control. When this line is "On", the serial
                         port is requesting that the modem send data.

                         A second use for this line is to provide
                         additional power to the "line powered" modems as
                         discussed in the paragraph above. You can use the
                         "RTS" utility provided with PortInfo to control
                         the RTS line.




























                                          24





               Copyright 1993, Computer Telecommunication Systems, Inc.





          6.0 The Other Utilities

          There are a number of additional utilities provided with
          PortInfo. These utilities are very specific in nature, and are
          provided to give you a standard user interface and source of
          support. You can also use these utilities to test the PortInfo
          utility.


               6.1 BUFFER

               BUFFER controls the internal buffer in a 16550A or
               compatible serial port. You can use this utility to turn the
               FIFO buffer "On" with any of the four ( 1, 4, 8, and 14)
               valid receiver trigger levels, or to turn the buffer off. In
               general, application software which can support a 16550A
               UART will control the buffer correctly. 

               The primary use of this utility is to: 1) turn off a 16550A
               buffer which was not turned off by an application; and 2) to
               provide a way to adjust the buffer setting for a software
               application which has the trigger level set too high. 

               If you have old software which does not support a 16550A,
               and you are experiencing an occasional overrun error (this
               often appears as a retry during a file transfer with an
               "error-free" connection), then you can try turning the
               buffer on with different trigger levels. This is an
               experimental process, and it may not work. In fact, it's
               possible your communication software will "lock up" if you
               do this. 

               From the DOS prompt, type "BUFFER" or "BUFFER /?" to display
               the command line options and examples. 

               NOTE: If no trigger level is specified on the command line,
               BUFFER will set the receiver trigger level to 14.













                                          25





               Copyright 1993, Computer Telecommunication Systems, Inc.





               6.2 COM_FMT

               COM_FMT sets the character format on a serial port to the
               specified value. You can use this to replace the MODE
               command provided with DOS on ports that DOS does not detect.
               The following chart shows the three character "format" value
               used on the command line and the associated description:

                    Format         Description
                      8N1          Eight data, No parity, 1 stop bit
                      8N2          Eight data, No parity, 2 stop bits
                      7E1          Seven data, Even parity, 1 stop bit
                      7E2          Seven data, Even parity, 2 stop bits
                      7O1          Seven data, Odd parity, 1 stop bit
                      7O2          Seven data, Odd parity, 2 stop bits
                      7M1          Seven data, Mark parity, 1 stop bit
                      7M2          Seven data, Mark parity, 2 stop bits
                      7S1          Seven data, Space parity, 1 stop bit
                      7S2          Seven data, Space parity, 2 stop bits

               From the DOS prompt, type "COM_FMT" or "COM_FMT /?" to
               display the command line options and examples.

               NOTE: most communication applications control this parameter
               directly and will change whatever you set with this utility.


               6.3 COM_BPS

               COM_BPS sets a serial port data rate (in bits per second, or
               BPS) to any of the common standard values supported by the
               serial port. You can use this to replace the MODE command
               provided with DOS on ports that DOS does not detect. The
               following data rates are supported by COM_BPS: 110, 300,
               600, 1200, 2400, 4800, 7200, 9600, 14400, 19200, 38400,
               57600, and 115200 bits per second (bps). From the DOS
               prompt, type "COM_BPS" or "COM_BPS /?" to display the
               command line options and examples.

               NOTE: most communication applications control this parameter
               directly and will change whatever you set with this utility.









                                          26





               Copyright 1993, Computer Telecommunication Systems, Inc.





               6.4 DOS_COM

               The BIOS of your computer system creates a list of detected
               serial ports when it boots. Unfortunately, many computers
               will only detect the standard serial ports COM1 and COM2.
               Some computers will look for the conventional COM3 and COM4
               ports as well. You can use the PortInfo summary screen line
               "DOS uses port as" to determine whether the BIOS has
               detected the serial port.

               DOS will only use ports that are detected in the BIOS list
               of serial ports. For example, DOS must know a COM3 port
               exists if you want to redirect LPT1 to COM3, where you have
               a serial printer. If PortInfo shows "DOS uses port as N/A",
               then you need to help it out and add COM3 to the list of DOS
               ports. You use DOS_COM to do this. From the DOS prompt, type
               "DOS_COM" or "DOS_COM /?" to display the command line
               options and examples.


               6.5 DOS_SWAP

               DOS_SWAP exchanges two port addresses in the list of serial
               ports used by DOS. From the DOS prompt, type "DOS_SWAP" or
               "DOS_SWAP /?" to display the command line options and
               examples. You can use the PortInfo summary screen line "DOS
               uses port as" to determine whether how your BIOS has
               assigned the serial ports it detected.


               6.6 DTR

               DTR controls the Data Terminal Ready line for the port
               specified. You can raise (turn "On") or lower (turn "Off")
               the DTR line with this utility. See the discussion on the
               DTR line in the section dealing with the PortInfo summary
               screen for applications of this utility. From the DOS
               prompt, type "DTR" or "DTR /?" to display the command line
               options and examples. 











                                          27





               Copyright 1993, Computer Telecommunication Systems, Inc.





               6.7 IRQ

               IRQ controls the interrupt request line (Out2) from the
               serial port specified. Generally, a serial port should have
               IRQs disabled (IRQ Status "Off" on the PortInfo screen) at
               all times except when the serial port is actually being
               used. The major exception to this rule is when a serial
               mouse is attached to the serial port. The mouse driver will
               enable the interrupt and keep it enabled at all times.

               If you want to try sharing an interrupt between a mouse and
               a modem, you can in some cases manage this with IRQ. For
               example, if you have a mouse on COM1 and a modem on COM3,
               both using IRQ 4, you can run IRQ to disable interrupts on
               COM1. Then run your communication program. When you are
               finished with your communication program, you can (but
               normally you don't have to) run IRQ to re-enable the COM1
               interrupt. 

               NOTE: this will NOT work reliably with a communication
               application that is "mouse aware". If you need to share an
               interrupt with a mouse-aware application, then you need to
               use a utility similar to the CTS "MouseOff" and "MouseOn"
               utilities.

               From the DOS prompt, type "IRQ" or "IRQ /?" to display the
               command line options and examples. 


               6.8 RESETCOM

               RESETCOM resets a serial port to the DOS default condition.
               Interrupts are disabled, the port is set to 2400 bits /
               second with a character format of 8 data bits, no parity,
               and 1 stop bit, and the Request to Send (RTS) and Data
               Terminal Ready (DTR) lines are set low. If the port is a
               16550A or compatible, the buffers (FIFOs) are also disabled.

               There are a few communication applications which do not
               properly restore a serial port after completion. ResetCOM
               can be used to completely reset the serial port to a well-
               defined state.

               From the DOS prompt, type "RESETCOM" or "RESETCOM /?" to
               display the command line options and examples. 





                                          28





               Copyright 1993, Computer Telecommunication Systems, Inc.





               6.9 RTS

               RTS controls the Request to Send line for the port
               specified. You can raise (turn "On") or lower (turn "Off")
               the RTS line with this utility. See the discussion on the
               RTS line in the section dealing with the PortInfo summary
               screen for applications of this utility. From the DOS
               prompt, type "RTS" or "RTS /?" to display the command line
               options and examples. 









































                                          29





               Copyright 1993, Computer Telecommunication Systems, Inc.























































                                          30





               Copyright 1993, Computer Telecommunication Systems, Inc.





          7.0 PortInfo FAILURE and WARNING Messages

          The different types of failures and conflicts detected by
          PortInfo are separated into different categories. Each FAILURE
          and WARNING message can be referenced by number to the list
          below. Steps you can take to correct each of the problems are
          described.

          The general rule is to pay the most attention to the first
          FAILURE message that displays. Once a FAILURE has been detected,
          it should be corrected before looking at other problems that may
          be reported.


               7.1 Interrupt Conflicts

               An interrupt conflict message indicates that one or more of
               your serial ports is not always generating interrupts. This
               can cause a number of "interesting" problems that sometimes
               appear and disappear for no apparent reason. Finding the
               cause of the problem requires both a tool like PortInfo to
               identify that the problem exists, and patience on your part
               in taking a systematic approach to fixing the problem.
               Please follow the directions carefully.


                    7.1.1 Message PI-2010

                    Symptoms: You may have regular or sporadic lockups
                    using either of the ports at this address. 

                    Solution: As the message indicates, PortInfo is
                    detecting two separate interrupts when testing a single
                    serial port address. The typical cause of this is two
                    different serial ports at the same address (eg, two
                    separate UARTs defined as COM1). To fix this problem,
                    it is necessary disable, remove, or reassign one of the
                    serial ports to another address location. 












                                          31





               Copyright 1993, Computer Telecommunication Systems, Inc.





                    7.1.2 Message PI-2020

                    Symptoms: You will likely get a system lockup, a high
                    rate of CRC errors (file transfer retries) if using a
                    modem, a very jerky motion on a serial mouse, or a
                    combination of these symptoms if you do not resolve
                    this problem.

                    Solution: If your software allows use of another port
                    or IRQ, then you can change the port settings to avoid
                    this IRQ. A second approach is to temporarily remove or
                    disable the serial port, and then to run a general
                    system diagnostic utility like Microsoft's MSD to
                    determine which other device is using the IRQ. Then you
                    can decide which one of the two will actually use the
                    IRQ.


                    7.1.3 Message PI-2100

                    Symptoms: You have a serial port that works sometimes,
                    but not all of the time. You may have any or all of the
                    symptoms listed for any message in the PI-2000 to PI-
                    2999 range.

                    Solution: The usual causes for this error message are
                    multiple serial ports at the same address, or another
                    device using the interrupt. Use the solutions described
                    for PI-2001 and PI-2002.


                    7.1.4 Message PI-2110

                    Symptoms: Most applications will lock up when trying to
                    use this port.
           
                    There are three common causes for this message.
                    Troubleshooting this problem requires a careful and
                    methodical approach. The basic idea is to reduce your
                    system to a state where the conflict is no longer
                    observed, and then add boards back in one at a time to
                    determine which board is involved with the conflict.
                    Often (but not always) the board you have most recently
                    added to your system is the culprit.

                    Diagnosing and repairing this problem often involves
                    opening your computer system and removing / installing
                    boards. Be sure to follow the instructions provided


                                          32





               Copyright 1993, Computer Telecommunication Systems, Inc.





                    with your computer system when adding and removing
                    boards. 

                    PortInfo is most useful at diagnosing problems if you
                    run it after installing each board. By making sure that
                    the system is ok after each board is added, you can
                    then quickly identify which board is causing the
                    problem.


                         7.1.4.1 You have multiple ports at the same
                         address

                         This is a common problem with many computers.
                         There is often a forgotten or unknown serial port
                         installed in the computer, and adding another port
                         at the same address location can cause all sorts
                         of interesting problems. The best way to approach
                         this problem is to remove all of the add-in boards
                         that have serial ports from your system. This
                         includes internal modems as well. Then run
                         PortInfo to verify that your system is no longer
                         displaying this error message. If the error still
                         exists, then it is likely due to one of the other
                         problems discussed here. If the problem did go
                         away, then add each of the boards back into your
                         computer one at a time to determine which board
                         causes the problem. 

                         After you have identified which board causes the
                         problem, you should change the serial port address
                         (or Com# setting) to a selection which not used on
                         your system.

















                                          33





               Copyright 1993, Computer Telecommunication Systems, Inc.





                         7.1.4.2 You have another device using the same
                         interrupt

                         Many different devices compete for interrupts with
                         your serial ports, including other serial ports
                         (including internal modems), bus mice, network
                         cards, sound cards, and so on to name several.
                         While well-behaved serial ports and software will
                         allow serial ports to share an IRQ, you generally
                         cannot share an IRQ between a serial port and
                         another device. Bus mice often use IRQs 2,3,4,5,
                         or 12, and sound cards commonly use IRQs 5 and 7.
                         Try removing these cards from your system and then
                         run PortInfo again to see if the problem still
                         appears. If the problem still exists, then leave
                         the boards out and continue diagnosing the problem
                         following the steps in (1). When you have the
                         system to the point where the error is no longer
                         reported, then begin adding your boards back to
                         the system one at a time, running PortInfo after
                         you've added each board to determine which board
                         is involved in the conflict.



                         7.1.4.3 Your system will not let you share this
                         interrupt

                         There are some computer system motherboards which
                         simply will not let any other device generate
                         interrupts for IRQs used on the motherboard. For
                         example, if you have a serial port on one of these
                         motherboards set to use Com1 / IRQ 4, no other
                         device will be able to use IRQ 4.

                         Your only solution, if you need to share these
                         interrupts to make everything fit, is to disable
                         the serial ports on the motherboard, and purchase
                         an add-in serial port card. CTS offers several
                         options, so be sure to give us a call.










                                          34





               Copyright 1993, Computer Telecommunication Systems, Inc.





                    7.1.5 Message PI-2200

                    This is an informational message regarding the Telcor
                    Systems T/Port card. A newer ROM exists for your
                    T/Port. If you are experiencing problems with the
                    T/Port, then you should contact Telcor Systems Inc. for
                    more information. 

                    NOTE: PortInfo is not able to test the IRQ used by the
                    T/Port when this message is displayed.


                    7.1.6 Message PI-2300

                    Symptoms: If you use well-behaved software, and if your
                    hardware allows sharing interrupts, then everything
                    will be fine. If not, then you can have problems
                    ranging from serial ports which work intermittently to
                    complete system lockups.

                    Solution: Make sure the hardware will allow the
                    interrupt to be shared among multiple devices, and that
                    your software will make the IRQ inactive on the board
                    it uses after it has completed use. You may not use two
                    devices at the same time on the same interrupt.


               7.2 Port Conflicts

               Port conflicts normally indicate that there are two serial
               ports located at the same address. This is commonly done
               when installing new serial cards or modems into an older
               machine without knowing for certain what equipment is
               already installed.
















                                          35





               Copyright 1993, Computer Telecommunication Systems, Inc.





                    7.2.1 Message PI-3000

                    Symptoms: System lockup or failure of a communication
                    application to successfully use a modem.

                    Solution: You definitely have a conflict between a
                    serial port and another device, possibly another serial
                    port, at the same address location. Remove or disable
                    the port which fails the test, and run PortInfo again.
                    If another port is reported at the same address, then
                    you have a conflict between two serial ports. If no
                    other serial port is detected at that address, then you
                    have a conflict with another device. Common conflicts
                    involve local area network cards.


                    7.2.2 Message PI-3100

                    Symptoms: Your system may lock up, or the display may
                    show meaningless characters ("garbage").

                    Solution: You cannot use a serial port at the normal
                    COM4 address location if this message appears. The
                    display adaptor on your video card is installed at the
                    address normally used for Com4.


               7.3 Mouse Conflicts

               PortInfo looks for conflicts between your mouse and your
               serial ports. Most conflicts are detected by the interrupt
               conflict tests. However, PortInfo also checks for possible
               future conflicts.


                    7.3.1 Message PI-4000

                    This is a WARNING message that your bus mouse is using
                    one of the IRQs normally used by the Com1 or Com2
                    serial ports. If you are not using this port for any
                    connections, then you will not have any problems. If
                    you do use Com1 and Com2 for your communications and
                    they are using the standard IRQs (Com1 / IRQ 4, Com2 /
                    IRQ 3), then you need to change the IRQ used by the
                    serial port or the bus mouse to resolve the conflict.





                                          36





               Copyright 1993, Computer Telecommunication Systems, Inc.





               7.4 DOS Port Assignments

               The DOS port assignments are determined by a data table that
               is created by your computer system BIOS when the system is
               powered up or reset. The BIOS detects the ports installed in
               your computer and places them in a data area for use by DOS
               and application software.

               Unfortunately, different BIOS implementations work
               differently, so there are often inconsistencies in how the
               serial ports are used. Many systems will only look for two
               comm ports, and no system looks for more than four. The BIOS
               also doesn't follow conventions in assigning a port at a
               particular address to the proper Com port number. To further
               confuse the issue, many applications do not use this data
               area because of the inconsistencies and address the ports
               directly by address. This leads to the situation where two
               different applications use the same device through
               "different" ports.

               The best general rule is to always install ports in
               sequential order...that is, do not skip a port number. Make
               the first port Com1, the second Com2, and so on.

               PortInfo attempts to make sense of what is in your data area
               so you can adjust, or at least understand what is going on.


                    7.4.1 Message PI-5000

                    Symptom: You've assigned the port speed with the DOS
                    "MODE" command, but it is changed by a DOS MODE command
                    to another port.

                    Solution: You've apparently run a utility to swap or
                    install additional serial ports into the BIOS data
                    area. It is usually best to restore the ports to their
                    normal locations after you use the application which
                    required the exchange. See the discussion on the
                    DOS_SWAP or DOS_COM utilities provided with the SPU
                    will do this.









                                          37





               Copyright 1993, Computer Telecommunication Systems, Inc.





                    7.4.2 Message PI-5010

                    Symptom: PortInfo does not detect a serial port that
                    your system detected. This can be caused by the
                    improper use of the DOS_COM (or similar) utility, or
                    you may have a non-standard serial port the PortInfo
                    cannot detect (at the time this manual was written,
                    PortInfo successfully detects all known ports).

                    Solution: Make sure that you do not have a utility that
                    is "installing" a non-existent port into the BIOS data
                    area. 


                    7.4.3 Message PI-5020

                    Symptom: You have a device that is accessed through a
                    serial port in one application, but has to be accessed
                    through a different serial port (or cannot be accessed)
                    in another application.

                    Solution: The problem is that the serial port indicated
                    is not in the correct location in the BIOS data table.
                    Causes for this include improper use of port
                    reassignment or installation utilities like DOS_SWAP
                    and DOS_COM, or you do not have your serial ports
                    installed in sequential order. You can fix the problem
                    by making sure that your ports are installed in
                    sequential orders, starting with Com1, and then
                    avoiding the use of the port installation/reassignment
                    software.


                    7.4.4 Message PI-5030

                    Symptom: You've just installed a new serial port, and
                    one or more applications cannot detect it. 

                    Solution: If your application uses the BIOS data area,
                    then you will need to install the serial port using the
                    DOS_COM or similar utility. Many BIOS implementations
                    do not detect Com3 and Com4 serial ports, so this is a
                    common problem. 







                                          38





               Copyright 1993, Computer Telecommunication Systems, Inc.





                    7.4.5 Message PI-5040

                    Symptom: You have a serial port installed that is not
                    detected one or more of your applications.

                    Solution: See the solution for PI-5030.


               7.5 Other CTS Software Detected

               The CTS Utility SwapIRQ can affect the reporting of IRQs
               used by some diagnostic software. PortInfo is "aware" of
               SwapIRQ and notifies you that it is still active.


                    7.5.1 Message PI-6000

                    Symptoms: Just an informational message to let you know
                    that SwapIRQ was detected and temporarily disabled by
                    PortInfo. The PortInfo reports will not be affected by
                    the presence of SwapIRQ.

                    Solution: You should disable SwapIRQ when your
                    application has finished with it by using the "/D"
                    command line switch.

























                                          39





               Copyright 1993, Computer Telecommunication Systems, Inc.























































                                          40





               Copyright 1993, Computer Telecommunication Systems, Inc.





          8.0 Customer Support Policy

          Customer support is provided via telephone, fax, and electronic
          mail. We provide from 30 to 90 minutes of support (depending on
          the license you obtained) for any registered user within the
          following guidelines:

          1. We cannot return phone calls for product support. However, if
          you leave a detailed message, we will reply via fax, electronic
          mail (E-mail), or regular mail. 

          2. Messages sent to us on CompuServe E-mail will usually receive
          a reply within 24 hours. 

          3. We will be happy to assist with SPU installation problems
          before you register. However, we cannot provide technical
          assistance until we've actually received your registration. We
          can register you over the phone via credit card if you need
          immediate assistance.

          Be prepared to answer the following questions before you call for
          assistance:

            *  The version number of your CTS Serial Port Utilities. You
               can view this information in the program title by starting
               any of the utilities. 

            *  The brand name and model number of your computer.

            *  What equipment you have in your computer. A general purpose
               diagnostic program such as Microsoft's MSD can be helpful in
               determining what other equipment is installed.

            *  The version of DOS you are using (type "VER" at the DOS
               prompt).

            *  A complete description of the problem.

            *  Can you duplicate the series of steps that results in the
               problem?

            *  Did an error message appear? What did it say?

          You may contact CTS via voice phone at 404-263-8623 during normal
          business hours (Eastern Time Zone), or 24 hours / day via FAX at
          404-263-0124, and on CompuServe at 76662,2315.




                                          41





               Copyright 1993, Computer Telecommunication Systems, Inc.























































                                          42





               Copyright 1993, Computer Telecommunication Systems, Inc.





          9.0 About Computer Telecommunication Systems

          Computer Telecommunication Systems, Inc. was formed in 1990 to
          provide new communication software products, custom programming
          services, and consulting on personal computer asynchronous
          communications. We currently offer (as of November, 1993) the
          following products and services:


               9.1 AT Command Test 

               AT Command Test (ATCT) is a software application that
               performs a comprehensive test of the AT command set of any
               modem claiming to be "Hayes Compatible". ATCT tests most of
               the standard modem commands, all result codes, and many
               other characteristics. ATCT provides three different reports
               of command set compatibility with nine different Hayes modem
               product lines. 

               ATCT is used today both as a qualification tool for
               purchasing modems by major corporations, and as a diagnostic
               tool for testing modems returned to corporate support
               services prior to obtaining warranty service. 

               Contact CTS for more information.


               9.2 SwapIRQ 

               A small utility that allows software to use IRQs that are
               not supported directly by the software. For example, a
               communication application that supports COM3 on IRQ 4 can
               now use COM3 on any IRQ. Or, a game that requires a sound
               card on IRQ 7 can now use a sound card that generates
               interrupts on IRQ 5. Contact CTS for more information.


               9.3 MouseOFF and MouseON

               MouseOff disables a serial mouse, allowing a modem or other
               device using the same interrupt (IRQ) to operate without
               interference. MouseOn re-enables the mouse after you have
               finished using the other device. MouseOff and MouseOn are
               especially useful in sharing an interrupt between a mouse
               and a modem when the communications software detects and
               tries to use the mouse. 




                                          43





               Copyright 1993, Computer Telecommunication Systems, Inc.





               9.4 Serial Cards (Comm Ports)

               We carry a variety of serial cards that contain 16550A or
               compatible UARTs. 


               9.5 Modems

               We carry most major brands of modems. Please call with your
               requirements.


               9.6 Fax / Modem / Phone Switches

               We carry fax / modem / phone switches from Command
               Communications, Inc., including the ASAP TF333 and ASAP
               TF555, as well as the distinctive ringing switch, the ASAP
               RD4000. 


               9.7 Surge Protection Devices

               We offer only the highest quality surge protection devices
               from APC, Panamax, and Tripp Lite which include equipment
               repair / replacement warranties and phone line protection
               for your fax or modem.


               9.8 Cables / Adapters

               We have a variety of serial cables, null modems, and 9 pin /
               25 pin adapters.

           
               9.9 Custom Programming Services

               Call us to discuss your special communications software
               requirements.


               9.10 New Products

               This manual may be several years old by the time you read
               this! Call us to see what's new!






                                          44