Installing TSX-Lite



      Installation of TSX-Lite is a simple process which  takes  about  10
      minutes.   The  installation process will create the TSX-Lite system
      directory, usually named TSX32SYS,  on  the  destination  disk.   It
      will  extract  the  TSX-Lite  system files from compressed libraries
      and write  them  into  this  directory.   The  TSX  kernel  program,
      TSX32.SYS,  will  be  copied to the root directory of your C: drive.
      When the installation is complete, your current  directory  will  be
      the  TSX-Lite  system  directory  on the destination drive.  The TSX
      installation process does not modify AUTOEXEC.BAT or CONFIG.SYS.

      The TSX-Lite  operating  system  coexists  peacefully  on  the  same
      computer  with  DOS.   To  start  TSX-Lite  you first boot DOS, then
      change to the TSX-Lite system directory  (usually  named  \TSX32SYS)
      and issue the RUNTSX command.

      See   Section  1.13  on  page  7  for  information  about  obtaining
      technical assistance.


      1.1 Hardware Requirements

      TSX-Lite requires a 386 or 486 based system with at least  4  MB  of
      memory.   VGA  and  MDA  display adapters are supported as well as a
      variety  of  disk  adapters.   Disk  compression  schemes  such   as
      DoubleSpace and Stacker are not supported.


      1.2 Disk Space Requirements

      After  installation,  the  distributed  files in the TSX-Lite system
      directory will occupy approximately 5 Mb.  In addition,  the  kernel
      file,  TSX32.SYS (which is always placed in the root of the C drive)
      will require about 1 Mb.

      However, when you  start  TSX,  a  virtual  memory  "page  file"  is
      created  in  the  TSX system directory which, by default, occupies 4
      MB of disk space.  The name of the page  file  is  PAGEFILE.TSX  and
      its  size  is  determined  by  the  TSX  system generation parameter
      PGFILSIZ.  The page file is used to hold the virtual memory  portion
      of  programs  that  are  not  currently present in main memory.  The
      PGFILSIZ parameter is discussed in the TSX-Lite documentation.   The
      total  required  disk space for a running TSX-Lite system is roughly
      10 megabytes.








                                       1


      1.3 Installation Modes

      TSX-Lite is distributed both on  floppy  disks  and  via  electronic
      distribution.   In either case, you will run an installation program
      which will:

        . Create the TSX-Lite directory on your hard disk.

        . Decompress the TSX-Lite files into that directory.

        . Ask you a series of questions about your system,  and  create  a
          configuration  file  based  on  your  answers  and  what  it can
          automatically detect about your system.


      1.4 Floppy Disk Installation

      If you received TSX-Lite on floppy disks, you  are  ready  to  start
      the  installation.   Simply  insert Disk #1 in drive A or B and type
      the command

          x:INSTALL

      where x is either A or B depending on which diskette drive  you  are
      using.

      Now  proceed  to  Section  1.6  which  describes  the details of the
      installation process.

      When the installation is finished, the TSX-Lite documentation  files
      will   be   stored   in   the  TSX32SYS  directory.   To  print  the
      documentation, simply type PRINT *.DOC after booting  TSX-Lite  (the
      TSXLITE.DOC manual is about 175 pages long).


      1.5 Installation from ZIP Files

      If  you  downloaded  TSX-Lite from a bulletin board, you should have
      four files with an extension of .ZIP.  The first file in the  series
      contains  the  TSX-Lite  documentation, and is much smaller than the
      others.   You  may  wish  to  download  this  file  and   read   the
      documentation before downloading and installing TSX-Lite.

      You   will   have   to   "unzip"  these  files  before  running  the
      installation program.  To do this, use the PKUNZIP utility  program.
      If  you  do not have a copy of PKUNZIP, you can download it from the
      same bulletin board where you got TSX-Lite.  Note, each of the  four
      .ZIP  files  contains a file named FILE_ID.DIZ.  These files provide
      descriptive information for bulletin boards  but  are  not  used  by
      TSX-Lite.

      To  unzip  the files, create a temporary directory on your hard disk
      and "CD" to that directory.   Now,  copy  all  .ZIP  files  to  that
      directory.  Then, type the command



                                       2


          PKUNZIP -O *

      You  should  now have the following files in the temporary directory
      in addition to the ZIP files:

          INSTALL.EXE      ! The installer program
          TSX-32.001       ! TSX-Lite compressed file #1
          TSX-32.002       ! TSX-Lite compressed file #2
          TSX-32.003       ! TSX-Lite compressed file #3
          TSXLITE.DOC      ! The TSX-Lite documentation
          REGISTER.DOC     ! TSX-Lite registration information
          INSTALL.DOC      ! This file
          READ.ME          ! Basic information about TSX-Lite
          FILE_ID.DIZ      ! Information file for BBS sysops

      Now, simply type INSTALL to start the  installation  program.   When
      you  have  completed  the installation, copy the documentation files
      to another directory, or print them out with the TSX command

      	PRINT *.DOC.

      You may then erase the files in the temporary directory.


      1.6 The Installation Program

      The Install program will display a  Main  Menu  with  the  following
      options:

          Install TSX-Lite
          Copy Individual Files
          Exit

      The  first option, Install TSX-Lite, will be highlighted, and is the
      appropriate one for all new  systems  and  system  upgrades.   Press
      Enter to select this option.

      If  you  make  an error any time during the installation process and
      wish to exit, simply  press  Ctrl-X.   You  may  then  re-start  the
      installation.

      If  this  is a new installation, the installation program will check
      the system for adequate memory and disk space, and  will  check  the
      CONFIG.SYS   file   for   possible  device  driver  conflicts.   The
      following types of drivers many  interfere  with  TSX-Lite  when  it
      begins  running:  Extended  memory  managers  such  as  QEMM.SYS and
      HIMEM.SYS;  disk  caching  programs  such  as   SMARTDRV.SYS;   disk
      compression programs such as DBLDISK.SYS and Stacker.

      If  your  system contains multiple hard disks, the program will then
      display a menu of available drives for you to select where you  wish
      to  install  TSX-Lite.   Use  the cursor keys or press the letter of
      the drive you select, then press Enter.  The selected  drive  should
      have  at  least  11  Megabytes  free.  The hard drive choices are as
      follows:


                                       3


        . Standard  AT  -  This  is  the  most  common  catagory  of  disk
          controller,  and includes ISA-bus, EISA-bus, and IDE controllers
          as well as ESDI and MFM/RLL.  If in doubt, select this option.

        . Adaptec 1540 SCSI - Includes the 1542 and compatibles,  and  the
          EISA 1742 in standard mode.

        . Adaptec  1740  SCSI/Enhanced  mode  - Select when using the 1742
          controller in enhanced mode.

        . Western Digital 7000 SCSI - This includes the  FAAST  family  of
          controllers for ISA and EISA machines.

        . Unisys/Convergent  SCSI - a proprietary controller found only on
          Unisys machines.

        . Standard PS/2 - This is the standard  controller  provided  with
          most IBM PS/2 machines.

        . PS/2 SCSI - This is the IBM SCSI controller for the PS/2.

      You  will  now  be  asked a series of questions to determine whether
      certain detached jobs should be started at system bootup.  The  jobs
      which  may  be  started  are  the print spooler and the window print
      facility.  Reply "Y" for each job your system will  require.   These
      selections  can  be changed later by using the TSGEN program.  If in
      doubt about an option the safest choice is "Y".

      The installation  program  will  now  begin  extracting  files  from
      compressed  libraries  and  copying them to your selected hard disk.
      Please do not interrupt this process until it is finished.

      After all files are copied, the installation process will  create  a
      file   named  TSX32.GEN  in  your  TSX-Lite  system  directory  with
      information about your configuration and choice of  options.   Then,
      the  TSGEN  program will run, applying the GEN options to the kernel
      file, C:\TSX32.SYS.  The TSX-Lite manual explains how  you  can  use
      TSGEN to customize and optimize TSX-Lite for your needs.

      The  installation  procedure checks for the presence of the COM1 and
      COM2 serial ports and defines them as TSX devices TTB0 and  TTC0  if
      they  are  present.   See the TSXLITE.DOC file for information about
      setting up COM3 and COM4 ports.


      1.7 Starting TSX-Lite

      Since TSX-Lite is an operating system and must have full  access  to
      the  computer  when  it  starts  running,  some  TSR programs or DOS
      device drivers may interfere with it.   In  particular,  you  should
      remove  any  of  the  following  programs  and/or  drivers from your
      CONFIG.SYS  and  AUTOEXEC.BAT  files  and  reboot  before   starting
      TSX-Lite:




                                       4


        . Memory  managers  such  as QEMM.SYS and HIMEM.SYS.  TSX-Lite has
          its own virtual memory manager built into it.

        . Disk compression schemes such as Stacker or DoubleSpace.   Note:
          TSX-Lite  does  NOT  support  disk  compression  and if you have
          compressed  your  disks  you  will  need  to  decompress  before
          starting TSX-Lite.

        . Disk caching programs such as SMARTDRV.SYS.

      When  the  installation  procedure completes, make sure your current
      directory is the TSX-Lite system directory (normally  TSX32SYS)  and
      type  RUNTSX  to  start  TSX.   A  screen will appear displaying the
      progress of the  bootup  process.   When  system  initialization  is
      finished  (it  takes  15  to  30 seconds), you will see the TSX-Lite
      greeting and a system prompt.   To  return  to  DOS,  type  the  TSX
      "SHUTDOWN" or "BOOT" commands.

      If  the  TSX-Lite  start-up  process  fails,  save  a  copy  of your
      CONFIG.SYS and AUTOEXEC.BAT files, create minimal ones  without  any
      TSR's  or  unnecessary device drivers, reboot, and then try to start
      TSX-Lite again.  See Section 1.12 for  solutions  to  some  possible
      problems.


      1.8 Using TSX-Lite

      When  TSX-Lite  starts it prints a welcome message and then displays
      a command prompt.  At this point you may type TSX  commands  or  run
      your  own  application  programs.   You may want to try a few of the
      following commands to get a  feeling  for  the  system:  "TSXSHELL",
      "HELP",   "SYSMON",   "FMAN",   "SHOW  SYSTEM",  "SHOW  USE",  "SHOW
      TERMINALS",  "SHOW  MEMORY",  "SHOW  PAGING",  "SHOW  CACHE",  "SHOW
      FILES", "SHOW FSTATUS", "SHOW ERRORS".


      1.9 Documentation Files

      The  following  documentation files are provided with TSX-Lite.  See
      the  REGISTER.DOC  file  for  information  about  purchasing   other
      manuals.

      TSXLITE.DOC  -- Reference manual for TSX-Lite.
      REGISTER.DOC -- Registration information and order form.
      INSTALL.DOC  -- Installation instructions.
      README.DOC   -- Basic introductory information.
      VENDOR.DOC   -- Information for vendors.


      1.10 System Upgrades

      The  installation program will detect if TSX is already installed on
      the target drive.  If so,  you  will  not  be  asked  the  questions
      mentioned  above  and  the  new files will simply be copied over the
      old ones.


                                       5


      Certain files which  are  considered  "user-specific"  will  not  be
      overwritten.   These  include  the  GEN file, startup command files,
      etc.  A list of these files will  appear  on  the  screen  (see  the
      following  section  for  a complete list).  If you wish any of these
      files to be replaced, press Ctrl-X  to  exit,  delete  the  file(s),
      then restart the installation program.


      1.11 Copy Individual Files Installation Option

      Use  this  option  to  copy  one  or  more  selected  files from the
      distribution disks.  Because files are stored  on  the  distribution
      disks  in  compressed  format,  they cannot be copied to your system
      with the COPY command.

      When you select this option, you will be prompted for the name of  a
      file  to  copy.  Type the filename and extension only, with no drive
      or directory specification.  Press Enter to continue.  You will  now
      be  prompted for another file to copy.  You may continue to enter as
      many files  as  you  wish  in  this  way.   Wildcard  filenames  are
      acceptable.

      Simply  press  Enter  without entering a filename when you are done.
      All files you selected will now be copied to the TSX-Lite  directory
      on  your  system.   If  you asked for the file TSX32.SYS, it will be
      copied to the root directory on drive C:.

      Certain  files  are  known  by  the  Installation  program   to   be
      user-modifiable.   The  Installation  program  will  not  copy these
      files to your hard disk if another file with the same  name  already
      exists.   To get a new copy of these files, you must first erase the
      original copy.  The files in this category are as follows:

         START.CMD
         LSTARTUP.CMD
         LSHUTDOWN.CMD
         STARTQUE.CMD
         QINIT.CMD
         E32.INI
         KERMIT.INI
         *.KEY


      1.12 Possible Installation Problems

      1.  During the installation process, a message appears of  the  form
          "We  had  a  problem reading a file." This indicates a corrupted
          compressed distribution  library  file.   Please  obtain  a  new
          distribution.

      2.  During  the  execution  of  the TSGEN program (immediately after
          the installation program "farewell" screen), an "out of  memory"
          message  appears.   TSGEN  requires  a substantial amount of DOS
          memory.  It cannot use EMS  or  XMS.   Remove  all  drivers  and



                                       6


          TSR's  from  your CONFIG.SYS and AUTOEXEC.BAT files, reboot, and
          try again.

      3.  The TSX boot process fails with a message  of  the  form  "error
          opening  keyboard  monitor."  This  indicates that TSX is having
          trouble finding its files on  the  hard  disk.   Run  the  TSGEN
          program,  select  "Set  Tuning  Parameters",  then  select  "All
          Parameters".  Press the  letter  "S"  and  scroll  down  to  the
          parameter  SYSDEV,  then  press enter.  This parameter tells TSX
          where its files are stored.

          The disk drive is specified as DHxy:  where  'x'  indicates  the
          disk  (a  letter)  and 'y' indicates a partition on that disk (a
          number).  So, for example, the C drive is always DHA0:.   The  D
          drive  may  be  either  DHA1:  if it is the 2nd partition on the
          first disk, or DHB0: if it is the 1st partition  on  the  second
          disk.   Verify  that  the  SYSDEV parameter contains the correct
          disk name.  See the TSX-Lite documentation for more  information
          on running the TSGEN program.

      4.  The  boot process fails with a message of the form "Error moving
          data" or "Error allocating memory."  This  usually  indicates  a
          conflict  with  a  DOS  memory  manager  or  device driver.  Try
          removing all such drivers from the CONFIG.SYS  and  AUTOEXEC.BAT
          files  and rebooting the computer.  If the problems persist, try
          running the CMOS setup program for your computer  and  disabling
          all ROM and video shadowing.

      5.  The   boot  process  completes  successfully  and  the  greeting
          message appears on the screen, but  the  system  appears  to  be
          "dead."  This  symptom  may  occur  when  TSX  has had a problem
          initializing the keyboard.  Reboot  the  computer  and  run  the
          TSGEN  program.   Select  "Set  Tuning  Parameters", then select
          "Console Keyboard Parameters".  Increase the value of  KBDELAY1,
          KBDELAY2,  KBDELAY3,  and  KBDELAY4  to 30000 (thirty thousand).
          Exit  TSGEN  and  try  running  TSX  again.   See  the  TSX-Lite
          documentation   for   more  information  on  running  the  TSGEN
          program.

      6.  The screen goes blank  after  entering  the  RUNTSX  command  to
          start  TSX.   TSX  is  having a problem with your video adapter.
          Try setting the adapter to its most basic mode and  try  booting
          again.


      1.13 Telephone Support

      If  you  need assistance installing TSX-Lite you are welcome to call
      the S&H support team.  The fee for this service is $1.50 per  minute
      which  may  be  charged  to  a Visa, MasterCard, or American Express
      credit card.  There is a $10.00 minimum charge for each  call.   The
      S&H support number is 615-327-3670.





                                       7