vFAST v1.0
             Copyright 1994 (c) International TeleCommunications
                              All Rights Reserved

                                 Introduction

         vFAST  was designed specifically for v32, v32bis,  and  vFAST
         modems. You should not attempt to use vFAST with a 2400  baud
         modem  unless your modem is error correcting.   The reason, a
         single  error could produce a resend request for as  much  as
         8192  bytes. It COULD be as little as 256 bytes but the  risk
         of 8192... well that is up to you.

         vFAST needs ONE of the following:

         16550 Uart
         Intelligent Digiboard (2, 4, 8, or 16 port).
         Intelligent Stargate.
         Intelligent Arnet.

         If you don't have one of the above, well try  and see.   You
         MIGHT be able to keep up but I doubt it.

         vFAST  is just what the name implies, a vERY  FAST  protocol,
         it'll run circles around Zmodem.

         vFAST  uses  DUAL 16 bit CRC's to protect  data.  Each  SHORT
         block  of  data  has a 16 bit CRC and every  8192  bytes  has
         another 16 bit crc. In short, CRC's inside of CRC's. Just  as
         effective  as  one single 32 bit crc but has  much  less  CPU
         overhead.

         vFAST  has RESTART recovery for aborted transfers as well  as
         SKIP for files you ALREADY have.

         One  way  to BOOST speed and cut down on CPU overhead  is  to
         reduce  SCREEN writes to a bare MINIMUM. We'll only show  you
         enough  data on the screen to let you know what is going  on.
         We'll only update the screen, unless an error occures,  every
         8192 bytes.

         You can ABORT a transfer by pressing ESC. Again, to keep  CPU
         overhead  low, we only check the  keyboard every  8192  bytes
         so  there may be a short delay  between  the time  you  press
         ESC and the program acknowledges the ESC.

         Once you see the acknowledgment, nothing may appear to happen
         for upwards of 10 to 12 seconds. vFAST is attempting to clear
         out the RX buffer and phone lines before exiting, to  prevent
         garbage  from spraying all over your screen.

                             Command Line Switches

         vFAST supports the following command line switches:

         -Tx            Use Timeslicing when you cannot send or
                        receive anything. x is the TYPE of time
                        slicing. Valid TYPES are:

                        D         Desqview
                        O         OS-2
                        W         Windows

                        If  you use OS-2 or Windows Time Slicing,  you
                        must have have  DPMI turned on.

         -Bxxxxx        xxxx is the connect baud rate.

         -Pxxx          xxxx is the serial port, 1-4 if using the
                        standard internal driver.

         -Lxxxx         xxxx is Serial LOCK rate, 9600 - 115200.

         -S  <Fnames>   Start Sending files. Fnames is the  names  of
                        the  files  to  send.  Each  name  should   be
                        separated  by a single blank space. If  Fnames
                        is  prefixed  with an AT sign, @,  vFAST  will
                        ASSUME  Fnames is the name of a  SEND  control
                        file.

                        E.g.  -S @C:\TERM\SEND.CTL

                        SEND.CTL would be a text file listing the
                        files to send, one per line. Drive, path,
                        and DOS wildcards supported.

                        This must be the LAST command line switch used.

         -D<TYPE>       The TYPE of serial driver to use. Valid <TYPE>
                        are:

                        D       Digiboard
                        S       Stargate
                        A       Arnet

                       The default is the internal (Standard DOS  type
                       serial ports) highspeed serial driver.

         -N*N          If you're running vFAST as a protocol driver
                       with Osiris XLT, include this switch.


         -R            Begin Receiving, must be the LAST command line
                       switch used.

         -K            Disable Keep Aborted Transfers. The default it
                       to keep all partial transfers. If you use this
                       driver as an external protocol driver for a BBS
                       you'll  want  to include this  on  the  command
                       line.

         -U<PATH>      This tells vFAST to place all files you receive
                       in   THIS  directory.  This  feature  is   ONLY
                       available if you register vFAST.

         The  minimum  command  line for RECEIVING  a  file  would  be
         something like this:

         vFAST -B<BaudRate> -L<LockRate> -P<Port Number> -R

         The  minimum  command  line  for  SENDING  a  file  would  be
         something like this:

         vFAST -B<BaudRate> -L<LockRate> -P<Port Number> -S <Ctl Filename>

         Notice that I assumed a LOCKED serial port.

         Example of an Osiris XLT Rcv cmdline:

         VFAST -B*B -L*L -N*N -P*P -K -R

         Example of an Osiris XLT Send cmdline:

         VFAST -B*B -L*L -N*N -P*P -S @*U

                                   Shareware

         vFAST is shareware. Meaning you can use it for up to 30  days
         without  registering  it. When you finish your  download,  or
         uploads,  the  shareware version will pause for  60  seconds.
         Registering  vFAST  removes  this delay and  enables  the  -U
         switch.

                                  (Cut Here)
         -------------------------------------------------------------

                               vFAST Order Form

         Send $15.00 (US Currency) to:

                       International TeleCommunications
                                302 W. Mckinley
                          Poplar Bluff Mo. 63901-6372
                           United States Of America


         Register To (___________________________________)


         A  registration key will be placed on our BBS at  (314)  686-
         0120 for you. The key will be password protected so only  YOU
         can download it. What Password do you want to use?

         Password (________)

         ____________________________________________________________
                                  (Cut Here)