Program STSORBIT PLUS

               Space Shuttle and Satellite Orbit Simulation

                       With Multi-Satellite Tracking


               (Enhanced Version for 286/386/486 Computers)







               (C) Copyright David H. Ransom, Jr., 1989-1993
                           All rights reserved.





                               Version 9338
                            September 15, 1993




                          by David H. Ransom, Jr.
                   Rancho Palos Verdes, California, USA




                          Bulletin Board Systems
                          ----------------------

                             RPV ASTRONOMY BBS
                   (310) 541-7299 @ 14400/9600/2400 Baud

                              RPV HOTLINE BBS
                      (310) 544-8977 @ 2400/1200 Baud

Program STSORBIT PLUS Satellite Orbit Simulation                  Page ii


                             TABLE OF CONTENTS

INTRODUCTION ......................................................1
HARDWARE AND SOFTWARE REQUIREMENTS ................................6
PROGRAM DESCRIPTION ...............................................7
STSORBIT PLUS FILES ...............................................9
STSPLUS MAP PROJECTIONS AND DATABASES .............................12
PROGRAM SETUP AND USAGE NOTES .....................................14
  DOS 5.0 CONFIG.SYS Setup ........................................14
  Using a RAM Disk ................................................15
  Copying Files for STSORBIT PLUS .................................16
  Slow Computers and 80x87 Math Coprocessor Chips .................17
  Starting Program STSORBIT PLUS ..................................19
  Predicting Visible Satellite Passes .............................20
    Predicting Satellite Passes with STSPLUS ......................21
    Predicting Satellite Passes with TRAKSTAR .....................23
  Printing Graphics Screens .......................................26
  Known STSPLUS Problems and Bugs .................................26
Preparing 2-Line Elements using VEC2TLE by Ken Ernandes ...........29
PROGRAM OPERATION .................................................31
STSORBIT PLUS SATELLITE TRACKING FEATURES .........................33
  Orthographic Projection Maps ....................................33
  Rectangular Projection World Maps ...............................34
  Rectangular Projection Quadrant Maps ............................34
  Rectangular Projection Zoom Maps ................................35
  Location Maps with Isocontours ..................................36
  Tracking Station Maps with Isocontours ..........................36
  Location and Features Labels ....................................37
  Big Clock Options ...............................................39
  Satellite Motion Maps ...........................................39
  Satellite Position and Orbit Projections ........................40
  Satellite Visibility ............................................41
  User's Circle of Visibility .....................................41
  Spacecraft Circle of Visibility .................................42
  SUN and Solar Features ..........................................43
  TDRS and Real Time Satellite Features ...........................45
  Ground Tracking Stations and .TRK Files..........................47
  Event Timers and Audible Alarms .................................49
  Pausing the Ground Track Display (F6 Key) .......................52
  Switching between MET and T+Epoch ...............................52
  Using FAST Time (F4 Key) ........................................53
  On-line Help (F1 Key) ...........................................53
ACTIVE KEYS DURING GROUND TRACK DISPLAY ...........................55
STSORBIT PLUS MAIN MENU ...........................................58
  F1  Convert Keplerian Data to 2-Line Format .....................59
      Example Data Input and Output ...............................61
      Received Keplerian Orbital Data Form ........................63
  F2  Read/Update NASA/NORAD 2-Line Elements ......................64
      Update Current TDRS and Real Time Satellites ................64
  F3  Data Output and Pass Prediction Selections ..................68
      Setting up Position and State Vector Data Output ............71
      Setting up Tabular Pass Predictions .........................74
      Data Mode 1: Azimuth/Elevation Data Format ..................78
      Data Mode 2: Latitude/Longitude Data Format .................79
      Data Mode 3: Topocentric RA/DEC Data Format .................80

Program STSORBIT PLUS Satellite Orbit Simulation                  Page ii


      Data Mode 4: Ascending Node X-Y-Z State Vector ..............81
      Data Mode 5: X-Y-Z Cartesian State Vector, 2 Data Lines .....83
      Data Mode 6: X-Y-Z Cartesian State Vector, Comma Delim ......85
      Data Mode 7: X-Y-Z Cartesian State Vector, Labeled Data .....87
      Data Mode 9: Pass Predictions ...............................89
  F4  Calculate Satellite Positions with TRAKSTAR .................91
  F5  Set Launch Time and Date ....................................91
      Using File STSPLUS.LTD for Launch Date & Time ...............92
  F6  Set/Read/Save TDRS and Real Time Satellites .................93
      F1  Display/Modify Satellite Assignments ....................93
      F2  Save SCF Satellite Configuration File ...................96
      F3  Read SCF Satellite Configuration File ...................97
      F4  Clear Static and Real Time Satellites ...................97
  F7  Set FILENAMES and PATHS .....................................97
  F8  Set Program TIME and DATE....................................98
      F1 Restore System Date and Time .............................100
      F2 Set DOS System Clock .....................................100
      F3 Set Simulated Date and Time using Calendar Method ........101
      F4 Set Simulated Date and Time using MET ....................101
      F9 Display Current RIGHTIME Corrections .....................102
      F10 Set UTC OFFSET and DAYLIGHT Flag ........................102
  F9  DOS Shell ...................................................103
  F10 Set STSORBIT PLUS Program Options and Features ..............103
  ENTER  Resume Mission ...........................................103
  ESC    Quit STSORBIT PLUS and Save Current Mission ..............103
PROGRAM OPTIONS AND FEATURES MENU .................................105
  F1  Program STSORBIT PLUS Information ...........................105
  F2  Set New Local Coordinates ...................................105
  F3  Set Display Features ........................................107
  F4  Select Satellite Coordinates ................................107
  F5  Show Ascending & Descending Node Data .......................108
  F6  Set Map Projection and Size .................................108
  F7  Enable/Disable EVENT TIMERS .................................108
  F8  Enable/Disable Audible ALARMS ...............................109
  F9  Set UTC Time Offset and Daylight Flag .......................109
  F10 Enable/Disable Printer Logging ..............................110
SET DISPLAY FEATURES ..............................................112
  F1  Display LOCAL Circles of Visibility .........................112
  F2  Display TDRS and Real Time Satellites .......................112
  F3  Display Additional Map Grid Lines ...........................113
  F4  Display Tracking Stations ...................................113
  F5  Display Ground Track: DOTS/LINE .............................113
  F6  Display Spacecraft Circle of Visibility .....................114
  F7  Display South Atlantic Anomaly Zone .........................114
  F8  Display Terminator, Sun and Spacecraft Lighting .............114
  F9  Display Map Locations and Features ..........................115
  F10 Display Lakes and Rivers ....................................115
STSORBIT PLUS's Orbital Model .....................................116
Accurate Time and the Personal Computer ...........................118
  Methods for Setting DOS Time ....................................119
  Maintaining Accurate DOS Time ...................................120
  Programs TIMESET and RIGHTIME ...................................122
Computer Bulletin Board Systems ...................................126
STSORBIT PLUS Revision History ....................................128

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 1


INTRODUCTION
------------

     Program STSORBIT PLUS is an enhanced version of STSORBIT, my original 
orbital tracking and display program. As a general rule, a 286 or better 
computer (AT-class IBM compatible) is required. A math coprocessor chip is 
STRONGLY RECOMMENDED and will dramatically improve performance; the math 
coprocessor chip is REQUIRED for acceptable performance when using the 
orthographic projection. Some users report "usable" performance on an XT-
class machine WITH a math coprocessor. See the section HARDWARE 
REQUIREMENTS for additional information and discussion. The program is 
intended for use during Space Shuttle missions and for general satellite 
tracking using NASA/NORAD 2-Line Orbital Elements. One primary satellite 
and up to 32 additional "static" or "real time" satellites may be 
simultaneously tracked in real time on most computers. Both orthographic 
and rectangular map projections are available, displaying the Earth as a 
globe or the more traditional "flat" map. Tabular line-of-sight satellite 
pass predictions may be made from within STSORBIT PLUS and passes of 
interest may be easily displayed.
     STSORBIT PLUS is very accurate when used with current (and accurate) 
2-line elements. The program has been qualified by the USAF and meets the 
requirement of placing a satellite within 0.5 km over a 24-hour time span 
from the epoch time of the 2-line elements. It is used daily at the USAF 
Central Computer Complex at Cape Canaveral, by the DOD C-Band Radar Network 
at their worldwide radar sites, and at half a dozen NASA and aerosapce 
control centers around the country. The program is made available to school 
teachers through the NASA Spacelink BBS and the NASA Teacher Resource 
Centers. Numerous schools have made contact with the space shuttle via 
SAREX amateur radio while using STSORBIT PLUS.
     STSORBIT PLUS is copyrighted software; you are hereby granted a non-
exclusive license for non-commercial or educational use only. Agencies of 
the U.S. Government are also hereby granted a non-exclusive license for 
internal use. Use STSORBIT PLUS if you like it, discard it if you don't. 
There are no warranties of any kind. If you wish to use STSORBIT PLUS 
commercially, write for license information. The only request I make of 
users is that they take the time to complete and return the confidential 
questionnaire in file README. The questionnaire gives users a chance to 
offer comments and suggestions, and lets me know that people use and 
appreciate STSORBIT PLUS. Registration of STSORBIT PLUS is inexpensive and 
optional -- but will be appreciated and will encourage me to continue 
supporting and enhancing the program.
     Program STSORBIT PLUS (which I will usually refer to as STSPLUS from 
here on) is intended to display the position and ground track of an 
orbiting satellite on a selection of maps ranging from a full map of the 
world to zoom maps showing considerable detail. The program has special 
features implemented at the request of NASA astronauts and others for use 
during a NASA Space Shuttle mission. With the appropriate 2-line elements, 
STSPLUS displays the position and ground track of a variety of satellites 
such as the Space Shuttle, the Hubble Space Telescope, the Gamma Ray 
Observatory, or the Russian MIR Space Station. Accurate TDRS coverage, 
including times for acquisition and loss of signal, is calculated for 
satellites which use that satellite network for communications. Special 
Location and Tracking Station displays show concentric isocontours, circles 
of equal satellite altitude; these special maps can be especially valuable 
for visual or amateur radio sightings.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 2




                          **********************
                          *  IMPORTANT NOTICE  *
                          **********************

     After almost four years, I have discontinued support for the 
     simple orbital model first used in my original STSORBIT program. 
     The accuracy of that model is marginal at best and timely 2-line 
     orbital elements for space shuttle missions and other satellites 
     are now widely available. If you wish to use the simple orbital 
     model, use STSORBIT or a version of STSORBIT PLUS prior to 9240.

     Users who wish to convert space shuttle or satellite state 
     vectors to 2-line format should see the section "Preparing 2-Line 
     Elements using VEC2TLE" for a description of a program by Kenneth 
     Ernandes written specifically for this purpose. VEC2TLE has been 
     validated during several space shuttle missions and is highly 
     recommended.


     The initial premise for STSORBIT was to attempt to duplicate the wall 
map in NASA's Mission Control Center in Houston, Texas. Before I started 
this project, I had seen several other programs which tracked satellites 
but each fell short of my map and display objectives for one reason or 
another. I therefore set out to do the job myself. STSORBIT and now 
STSORBIT PLUS have been the result. Since then other programs have appeared 
which produce similar information, most notably Paul Traufler's excellent 
TRAKSAT (which was inspired by STSORBIT). It may be, of course, that others 
will judge this effort lacking for some tasks, but no one program can do 
everything. One problem is that of screen size and resolution: the wall map 
at Mission Control Center is some twenty feet wide with an impressive pixel 
resolution, very different from the typical personal computer monitor. The 
NASA wall map shows essentially the entire globe in a cylindrical 
projection; STSORBIT also used a cylindrical projection and restricted the 
vertical display to latitudes from +85 degrees to -85 degrees in order to 
achieve reasonable proportions and vertical resolution while at the same 
time showing recognizable land features. STSORBIT PLUS now presents the 
Earth as a globe using an orthographic projection with zoom while still 
retaining the original cylindrical (rectangular) projection. STSPLUS adds 
many additional features and improved accuracy over the original STSORBIT.
     Initially, and as a consequence of a lack of accurate orbital data for 
Space Shuttle missions while they were in progress, I did not try to be 
especially precise with respect to the orbital mathematics. Additionally, 
mathematical complexity had to be held to a reasonable minimum if older 
computers not equipped with a math coprocessor were to be able to maintain 
the presentation in real time. My somewhat casual attitude toward 
mathematical precision changed with the launch of the Hubble Space 
Telescope (HST) and the regular availability of US Space Command 2-Line 
Elements via modem from TS Kelso's Celestial BBS. Until HST, I had been 
content to manually adjust the orbital data occasionally during the course 
of a typical five day mission and live with the errors inherent in my 
original simple orbital model. The accuracy of that model degrades rapidly 
after five or ten orbits and, although it could be adjusted from time to 
time during a mission, more accurate data are now readily available prior 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 3


to a launch and during a mission. The NASA SpaceLink BBS in Huntsville, 
Alabama began posting 2-line orbital elements for the Space Shuttle in 
early 1991 due in part to my persistent and continuing requests; Bill 
Anderson, Jeff Ehmen, and Flint Wild, sysops of the SpaceLink BBS, are 
continually upgrading the services available.
     Beginning in mid-1990, therefore, STSORBIT was extensively modified to 
read orbital data from these USSPACECOM 2-line elements and thereby 
maintain significantly improved accuracy over long periods of time. As an 
incidental benefit, the ground tracks of other satellites (such as the 
Russian space station MIR) could also be displayed. At present, the orbital 
model (SGP4) used with 2-line elements is accurate only for low Earth 
orbits. Deep space orbits, defined as orbits having an orbital period 
greater than or equal to 225 minutes, require a more complex orbital model 
(SDP4) which takes into account solar and lunar perturbations for best 
accuracy. STSPLUS calculates data and displays a ground track for deep 
space objects but the accuracy of these data has not been validated; it is 
believed to be "reasonably" accurate. I plan to add the SDP4 orbital model 
to STSPLUS in a future release when time permits.
     At about the same time, STSORBIT also found its way to the NASA 
Johnson Space Center in Houston, Texas. Quite a few individuals from JSC 
sent me comments and suggestions for further improving the program, among 
them Ron Parise of the STS-35/ASTRO-1 crew. Ron suggested that I make 
modifications to allow the display of Mission Elapsed Time (MET) for 
shuttle missions while using the USSPACECOM 2-line elements. This would allow 
both the higher accuracy of the USSPACECOM 2-line orbital data and permit 
following the mission timeline using MET. Since launch time and date are 
not included in the 2-line elements but are required to compute MET, these 
data must be entered independently. Another suggestion from Ron and others 
was to include the Sun, solar terminator (calculated at Mean Sea Level), 
and spacecraft lighting conditions to determine if the spacecraft is 
visible.
     Not satisfied with the somewhat rough map used with STSORBIT (a 
digitized EGA world map), I upgraded the maps to use a modified version of 
the World Data Base II. This had the desired effect, to the point where 
rivers and other landmarks could easily be recognized on the monitor and on 
downlinked orbiter television. As a side effect, however, the processor 
overhead increased dramatically -- some slower computers not equipped with 
a math coprocessor were unable to keep up. I therefore essentially "froze" 
the original STSORBIT program (except for minor updates) and created this 
new program, STSORBIT PLUS, intended for the faster, more capable 
processors. Since mid-1991, STSPLUS has also spread throughout the various 
NASA Centers and around the world.
     In addition to NASA and individual users all over the world, STSPLUS 
and STSORBIT are also being used in an educational setting. As many as 1100 
high schools participated in the Inspire Project, a VLF propagation test 
flown on STS-45 and for which STSPLUS was one of the recommended tools. At 
a middle school in Kansas, the program is projected in the school 
auditorium from time to time during a mission to show the children 
graphically what is happening and to give them a sense of "real time" 
participation in our space program. At an Air Force training facility, 
STSORBIT is one of many tools used to prepare Air Force officers for their 
duties in the Air Force Space Command. The program was widely distributed 
at a recent National Association of Science Teachers convention and by 
radio amateurs at regional "ham fests". It is also available to educators 
through the NASA Teacher Resource Centers and the NASA Spacelink BBS.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 4


     In perhaps its most prestigious installtion, STSPLUS is the software 
used by the NASA/JPL Multimission Computer Control Center in Pasadena, 
California, to display the ground track of Earth-orbiting satellites. The 
Canadian Space Agency used STSPLUS as part of their briefing government 
officials during the STS-52 mission in October, 1992. Intelsat used STSPLUS 
operationally in May of 1992 at their Launch Control Center in Washington, 
DC, and at five tracking stations around the world during the exciting STS-
49 mission, the maiden flight of Endeavour and the rescue/reboost of the 
INTELSAT-VI satellite. Intelsat was kind enough to send me a letter saying 
that STSORBIT PLUS was "critical to mission success"! Numerous other 
official and semi-official installations use STSPLUS as the primary 
satellite tracking software or to supplement other software.

     A brief biographical note: I am a retired physicist and engineer who 
spent all of his professional life in the world of electronics, data 
communications and, more recently, computers. As a young man I was actively 
involved in the early American space program including projects such as 
Ranger, Mariner, Mercury, Gemini, and Apollo. Exciting times indeed! I 
spent considerable time at the Jet Propulsion Laboragory in the early 
1960's as a contractor on Ranger and Mariner; my respect and admiration for 
JPL and its people has, if possible, increased over the intervening 
decades. My interest in space has continued to this day. The desire to 
"keep in touch" with our Space Shuttle missions was one of the incentives 
in the development of this software. I continue to be astonished that a 
relatively inexpensive personal computer is sufficient to perform 
calculations that pushed the limits of our best mainframe computers only a 
decade or so ago. If STSORBIT PLUS also serves to help spark the interest 
of young people in science and technology or can be a learning tool at any 
level, I will have more than achieved my goals.

     No discussion of satellite tracking would be complete without thanks 
to Major T. S. Kelso, USAF, who almost single handedly brought satellite 
tracking within the reach of "ordinary folks". TS's Celestial BBS has been 
providing unclassified 2-line orbital elements direct from US Space Command 
(formerly NORAD, the North American Air Defense Command) at Cheyenne 
Mountain, Colorado, since 1986 or so. For many years, Celestial BBS was the 
only electronic source for orbital elements in the world. The Celestial BBS 
may be reached at (513) 427-0674 and is located near Dayton, Ohio. TS has 
also written a variety of satellite tracking software and his most recent 
program, TRAKSTAR, may be used directly from within STSPLUS to generate 
tabular data on upcoming satellite passes.
     Special thanks to Paul Traufler for his friendship and encouragement. 
Our regular telephone conversations have generated many a new idea and the 
synergism has been beneficial to us both. Our two programs, STSORBIT and 
TRAKSAT, have engaged us in a friendly rivalry which has, I think, improved 
both programs many fold. I may have provided the initial spur to Paul to 
write TRAKSAT (in order to improve on my "sloppy orbital math", as Paul 
described it) but TRAKSAT has in turn kept my nose to the grindstone and is 
recognized by many as the standard against which other satellite tracking 
programs are judged. The emphasis of the two programs is slightly 
different, with STSORBIT concentrating on the graphical display and TRAKSAT 
on high precision analytical and predictive techniques. I highly recommend 
TRAKSAT for the serious satellite tracker. My thanks as well for Paul's 
help in upgrading STSORBIT to use the USSPACECOM 2-Line Elements and other 
technical assistance.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 5


     Thanks also to Rob Matson and Joel Runes. Rob for offering comments 
and code to help me implement several of STSPLUS's more exotic features; 
Rob coined the phrase "isocontours" to describe the circle of equal 
satellite altitude around a location and his fine SKYMAP program generates 
high accuracy printed star maps with or without satellite tracks. And Joel 
for keeping us all up to date with current elements for space shuttle 
missions and his patience in testing innumerable beta versions of STSPLUS, 
thereby helping to track down some of the more subtle bugs.
     Finally, my thanks to all those individuals who have taken the time to 
write or leave a message on my BBS with comments and suggestions. While I 
haven't implemented every suggestion, many are now included and the 
feedback is most welcome.

     For individuals interested in our space program and who have access 
to a modem, I recommend NASA's SpaceLink Bulletin Board System in 
Huntsville, Alabama, (205) 895-0028, available twenty four hours per day, 
300 to 2400 baud. NASA SpaceLink, located at the NASA Marshall Space Flight 
Center and with 8 lines, provides a wealth of information on NASA and its 
projects. 2-line orbital elements for a Space Shuttle mission are usually 
available while the mission is in progress. In addition to educational 
materials and software (including my programs STSORBIT PLUS, STSORBIT and 
JPLCLOCK), general information on NASA programs and plans, news releases, 
and images from prior spacecraft missions such as Voyager, SpaceLink also 
devotes a complete section to current news and information on the Space 
Shuttle. I particularly appreciate the STS Mission Press Kit, posted about 
two weeks before each mission, which provides a great deal of information 
on the upcoming mission, payload and crew as well as broadcast schedules on 
NASA Select Television, Satellite F2-R, Transponder 13. Mission status 
reports are generated daily during the course of a mission. I regularly 
call SpaceLink and post files of interest on my own RPV ASTRONOMY BBS.
     For current Space Shuttle orbital information (if a mission is in 
progress), 2-line elements for more than 1,000 satellites, and the most 
recent versions of STSORBIT PLUS, STSORBIT, TRAKSTAR, TRAKSAT, and SKYMAP, 
call RPV ASTRONOMY BBS or RPV HOTLINE BBS (see title page for numbers and 
data rates available). The main system has well over 1,500 more or less 
regular users and is often busy, so please be patient. If you wish to 
receive STSORBIT PLUS (or any of my other programs) on disk, see file 
README for information.

                                   David H. Ransom, Jr.
                                   7130 Avenida Altisima
                                   Rancho Palos Verdes, CA 90274

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 6


HARDWARE AND SOFTWARE REQUIREMENTS
----------------------------------

     An AT-class computer equipped with a 286 processor (running at 8 MHz) 
and a 287 math coprocessor chip is the minimum system used for all program 
testing and development. While other systems may give acceptable 
performance, this minimum configuration assures that most features will 
execute as described and in real time. Performance with 386/387 and 486DX 
systems will be considerably superior to 286 systems. Note that NO TESTING 
is performed on systems not equipped with a math coprocessor chip. The 
following minimum hardware is recommended:

          286/386/486 IBM-compatible computer
          287/387/487 math coprocessor chip
          VGA color display
          Hard disk with up to 3MB available
          RAM disk with at least 500K space

     The 287/387 (and 487 for 486SX processors) math coprocessor chip is 
STRONGLY RECOMMENDED and is REQUIRED for acceptable performance. The 
calculations relating to orbital mechanics are very complex and STSPLUS 
will use the coprocessor if one is equipped; performance is improved by 
about an order of magnitude. Other "fast" processor and coprocessor 
combinations may yield acceptable performance. Math coprocessor chips are 
now reasonably inexpensive and the performance improvement is impressive 
and well worth the modest cost. As an example, my vintage Zenith laptop, 
equipped with an 80C88 processor and an 8087 math coprocessor, is just able 
to keep up in real time (rectangular modes ONLY!) when running at a clock 
speed of 8 MHz but the map drawing times are very slow. However, an 8 MHz 
286 computer without a math coprocessor does NOT provide reasonable 
performance; map drawing times are painfully slow.
     STSPLUS is intended to be used with an EGA or VGA video adapter and a 
color monitor; with these systems, the display is in color. Because of its 
improved vertical resolution, the VGA is recommended over the EGA. A 
monochrome display with shades of gray may also be used with the program 
(with the "/M" command line option). Because of hardware limitations, CGA 
and HGC systems can only present graphics in monochrome; although those 
display adapters are supported to some degree in current versions of 
STSPLUS, that support may NOT continue in future versions. The original 
STSORBIT will continue to support CGA and HGC monitors.
     A hard disk is required for performance reasons and for storage of the 
program, map databases and orbital elements files. A RAM disk with 
sufficient space to hold the various data files is also recommended for 
improved performace and to reduce wear and tear on the hard disk during 
periods of extended use.
     Although the program may execute properly on other software operating 
systems, STSPLUS has been designed and tested using standard configurations 
of Microsoft DOS 3.3 and 5.0. No optional Terminate and Stay Resident 
programs (TSR's) or "shell" programs have been tested except for Tom 
Becker's RIGHTIME. Third party memory management programs and Digital 
Research DRDOS may experience problems although some users report that the 
latest release of DRDOS 6.0 works correctly.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 7


PROGRAM DESCRIPTION
-------------------

     A typical Space Shuttle orbit is nearly, but almost never exactly, 
circular with an altitude of approximately 160 nautical miles to a maximum 
of approximately 300 nautical miles and an inclination of about 28 degrees 
through about 57 degrees. Occasional missions, especially military 
missions, fly at higher altitudes and/or inclinations and often use more 
elliptical orbits. Prior to 1990, little of this information was known to 
very good accuracy by the casual listener. Initially, therefore, the 
interested would-be mission observer may have only the time and date of 
launch and intended orbital altitude and inclination to initialize a 
tracking program. Given the geographical coordinates of the Kennedy Space 
Center and assuming a circular orbit, the data is sufficient to calculate 
at least a rough idea of the Shuttle's position for the first several 
orbits. After that, additional information was required if the position was 
going to be very close. This was the method used in my original STSORBIT 
program when 2-line orbital elements were not available.
     Estimated 2-line elements are usually available prior to a space 
shuttle launch and I usually post "adjusted" 2-line elements within two 
hours of a launch. "Real" 2-line elements from NASA or US Space Command are 
usually available 8 to 12 hours after launch. 2-line elements yield a more 
accurate position over longer time periods (provided no orbital maneuvers 
are performed). Using 2-line elements for any satellite is quite simple; no 
adjustment of orbital parameters is necessary. An abbreviated version of 
the 2-line element file available at the time of this release of STSPLUS is 
included in the distribution files; this abbreviated file contains 
approximately 150 satellites while the "full" file as posted on my BBS 
typically has more than 700 satellites. The data for each satellite is 
referenced to a specific date and time, the "Epoch" of the data. As a 
general rule, orbital calculations will be relatively accurate for 10 to 20 
days after the Epoch date; the lower the orbit, the greater the effect of 
factors such as atmospheric drag and the less accurate the calculations 
will be as time passes.
     STSPLUS displays a portion of the Earth using either an orthographic 
porjection (the Earth seen as a globe) or cylindrical projection (similar 
to the Mercator projection commonly used). The maps show most of the 
Earth's land boundaries and continental areas. Major oceans, seas, and 
rivers are easily recognizable. Considerable detail is shown at higher zoom 
factors. Automatic map generation ensures that the satellite is always 
displayed. The display shows the selected satellite as a small symbol or 
icon, the projected orbital ground track for the next three hours and the 
the past one and a half hours, and many other features including circles of 
visibility, TDRS coverage, and the solar terminator.
     Data is displayed which gives the current ground track position of the 
satellite, known as the "sub-satellite point", antenna or viewing angles, 
spacecraft lighting, TDRS communications coverage (when applicable), and a 
variety of other information. A selection of map modes and display features 
allow users to configure the program to meet their requirements.
     STSPLUS has been validated by the USAF and is approved for use on the 
Eastern and Western Ranges. It is sufficiently accurate (given current and 
accurate 2-line orbital elements, of course!) that the program is being 
used operationally by NASA, USAF, and Intelsat. Among the current users 
are:


Program STSORBIT PLUS Satellite Orbit Simulation                   Page 8


          NASA/JPL Multimission Computer Control Center, Pasadena, CA
          NASA/Lewis User Operations Facility, Cleveland, OH
          Rockwell Mission Control & Support, Downey, CA
          Aerojet Emergency Control Center, Sacramento, CA
          USAF Central Computer Complex, Cape Canaveral, FL
          DOD C-Band Radar Network, worldwide radar sites

In addition to these official or semi-official users, thousands of amateur 
radio operators and "just plain folks" all over the world use STSPLUS to 
track the space shuttle and other satellites.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 9


STSORBIT PLUS FILES
-------------------

     STSORBIT PLUS is normally distributed via bulletin board systems in 
archived form using the ZIP format by PKWare. Note that all files (except 
map databases) for STSORBIT PLUS are called "STSPLUS" in order to conform 
to DOS filename requirements and to avoid confusion with the similarly 
named files for the original STSORBIT. The following files are usually 
included (files marked with "*" are available separately):

          STSPLUS.EXE        Main STSPLUS Program     (required)
          STSPLUS.DOC        Documentation            (not required)
          STSPLUS.ICO        Icon for WINDOWS 3       (optional)
          STSPLUS.KEY        STSPLUS Active Keys      (optional)
          STSPLUS.LOC        Map Locations & Features (optional)
          STSPLUS.LTD        Satellite Launch Dates   (optional)
          STSPLUS.SCF        Satellite Config File    (optional)
          STSPLUS.TRK        NASA Tracking Stations   (optional)
          STSPLUS.CTY        City Coordinates         (optional)
          STSPLUS.INI        Initialization data      (see below)

          EARTH4.MCX         Level 4 Map Index        (required)
          EARTH4.MCP         Level 4 Rect Map Data    (required)
          EARTH4.XYZ         Level 4 Ortho Map Data   (required)

          EARTH3.MCX         Level 3 Map Index        (optional) *
          EARTH3.MCP         Level 3 Rect Map Data    (optional) *
          EARTH3.XYZ         Level 3 Ortho Map Data   (optional) *
          EARTH2.MCX         Level 2 Map Index        (optional) *
          EARTH2.MCP         Level 2 Rect Map Data    (optional) *
          EARTH2.XYZ         Level 2 Ortho Map Data   (optional) *
          EARTH1.MCX         Level 1 Map Index        (optional) *
          EARTH1.MCP         Level 1 Rect Map Data    (optional) *
          EARTH1.XYZ         Level 1 Ortho Map Data   (optional) *

          MSHERC.COM         Hercules driver          (required for HGC)

          TLEnnn.TXT         2-Line Elements          (optional)

          NASA.TRK           NASA Tracking Stations   (not required)
          CIS.TRK            Russian Tracking Stations(not required)
          INTELSAT.TRK       INTELSAT Tracking Stns   (not required)
          SPACENTR.TRK       Other Tracking Stations  (not required)
          STSLNDG.TRK        Orbiter Landing Sites    (not required)

          README             STSPLUS Confidential Questionnaire
          QUICK.DOC          Quick Start Instructions

          SOP9311.ICO        Alternate STSPLUS Icon   (not required)

Files noted as "(required)" must be in the current default directory (or in 
a specified directory in some cases) for program operation. Files noted as 
"(optional)" are not required when STSPLUS is operated but provide 
additional features or information if present. In order to minimize the 
disk space required, all.EXE files been compressed with PKWare's PKLITE 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 10


Professional; these files require additional time to begin execution since 
they are decompressed "on the fly" at load time.

                          ***  IMPORTANT NOTE ***

     File STSPLUS.INI contains initialization data from previous runs 
     of the program. If file STSPLUS.INI is not present it will be 
     created. Note that if STSPLUS.INI was written by a version prior 
     to 9332, all data will be ignored and the program must be 
     initialized as if being run for the first time.


     STSPLUS can use map databases with different degrees of map detail. 
Level 4, required for operation, contains the minimum detail and Level 1 
contains the maximum detail. As noted in the list above, three files are 
used for each level of map detail: MCX files contain an index of the map 
data; MCP files contain map coordinates for rectangular projection; and 
XYZ files contain map coordinates for orthographic projection. STSPLUS 
checks for the levels that are present and uses the level appropriate for 
the zoom factor in effect or, if that level is not present, the maximum 
level that is present. Level 1 is checked first, then Level 2, etc. Level 4 
files MUST be present or an error message is displayed and the program 
aborts.

                          ***  IMPORTANT NOTE ***

     STSPLUS assumes that if a particular level of map database is 
     found, ALL lower levels of map database are present. Missing 
     levels of map database will cause a program error.


     File STSPLUS.KEY is a quick reference list of the keys that are 
active while the map is displayed and includes a brief description of the 
function of each key. It has been extracted from this documentation.
     File STSPLUS.LTD contains the launch date and time for selected 
satellites. The file may be updated when new satellite launch date and 
time data is entered via the program.
     Files with filetype .TRK are tracking station locations or other 
locations of interest which may be plotted on the map. These files may be 
created or edited with a standard ASCII editor. If you wish to use a 
different TRK file, use Function Key F7 from the Main Menu to select 
the desired file.
     File STSPLUS.SCF is a sample multiple satellite configuration file 
which may be used to display multiple TDRS and real time satellites. Up to 
16 additional satellites may be tracked using this feature.
     File TLEnnn.TXT (where "nnn" will be a number such as "153") is a set 
of USSPACECOM 2-line elements as of the date of the file. Note that the 2-
line elements should only be used for ten to twenty days after the epoch 
date for each satellite if reasonable accuracy is to be maintained. Current 
orbital elements are regularly posted on my bulletin board system and 
elsewhere. Other files with 2-line elements are also available; they 
typically have names like GSFCnnn.TXT or N2L-nnn.TXT for general 
satellites, and STSmmNnn.TXT for Space Shuttle missions. Space Shuttle 
orbital elements are usually posted at least daily during missions; because 
of orbital maneuvers, Space Shuttle elements more than 24 hours old may 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 11


yield inaccurate positions.
     File STSPLUS.LOC contains geographic coordinates and labels for 
selected locations and major oceans and seas. These labels may optionally 
be displayed on the maps. The file may be edited with a standard ASCII 
editor to add or delete locations and features. See the section "Location 
and Features Labels" for additional information.
     Other files, such as 2-line elements for an upcoming Space Shuttle 
mission or a mission in progress, may be included from time to time. Files 
with 2-line orbital elements normally have filetype ".TXT" or ".TLE". Some 
common satellite name abbreviations are:

          STS       Space Shuttle missions
          HST       Hubble Space Telescope
          GRO       Compton Gamma Ray Observatory
          UARS      Upper Atmosphere Research Satellite
          TOPEX     Topex/Poseidon Earth Resources Satellite
          ROSAT     Roentgen Satellite Observatory
          MIR       Russian Space Station

There are many other satellites for which data is available. US Space 
Command (formerly NORAD) currently tracks some 7000+ objects, of which data 
for more than 700 is usually included in the full TLEnnn.TXT files posted 
on my bulletin board system.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 12


STSPLUS MAP PROJECTIONS AND DATABASES
-------------------------------------

     Cartographers and navigators have long wrestled with the problem of 
map projections, the process of transferring location information from a 
sphere to a flat surface or map. The U.S. Geological Survey publishes "An 
Album of Map Projections", Professional Paper 1453, that contains some 90 
basic projections in over 130 different modifications and aspects. Each 
projection or modification was developed to serve some specific need or to 
optimize certain parameters. The primary concern with any map projection is 
distortion. For STSPLUS, this means the accuracy with which the selected 
portion of the Earth's surface is displayed. Naturally, the viewer desires 
accuracy in area, shape, and distance; unfortunately, you can't have all 
three simultaneously with a single map projection.
     The cylindrical or rectangular projection, used here and with the 
original STSORBIT program, is a good compromise where drawing speed is to 
be minimized. The map coordinate data translate exactly to screen pixels 
with a minimum of computer processing. However, this projection is unable 
to diplay the polar regions well; the distortion increases non-linearly as 
the latitude increases. I have chosen to limit the latitude to plus and 
minus 85 degrees to avoid some of the severe problems which occur very near 
the poles. As the magnification is increased, the distortion inherent in 
this projection is reduced for the area shown but different latitudes are 
displayed at different scales for a given magnification. A satellite 
appears to move more rapidly in high latitudes than at mid or equatorial 
latitudes.
     The orthographic projection views the world as a sphere and thus only 
a single hemisphere can be seen at any given time. However, since the map 
center may be placed at any desired point, the "hemisphere" may include a 
pole. The projection is calculated as if the viewer were at a great 
distance from the Earth and therefore can see a complete hemisphere. This 
makes the projection ideal for viewing high inclination satellite orbits. 
Perspective is not included in the projection calculations for simplicity. 
The orthographic projection has the advantage that ANY area of the Earth 
may be viewed, including the poles, and the scale remains the same for any 
given magnification and is independent of the area viewed. At the center of 
the map, circles of visibility appear as true circles; however, area 
distortion increases toward the edge of the screen and is especially 
noticeable when the full hemisphere is displayed.
     The map databases used for STSPLUS are an adaptation of the Micro 
World Database II ("WDB"), generously placed in the public domain by Peter 
Pospeschil and Antonio Riveria, and were produced in about 1986. The 
original data were from the U. S. Central Intelligence Agency (CIA) as 
distributed by the National Technical Information Service (NTIS). There are 
several known errors in the database: one island in the South Pacific is 
missing its northwestern portion, and several islands near the North Pole 
are classified as "lakes" instead of "islands" and are therefore rendered 
in the wrong map color. There are also numerous gaps in coastlines which 
make color fill very difficult over the range of magnifications used here.
     The original map data are identified by "level of detail" with Level 1 
having the greatest detail and Level 5 having the least detail. I have 
elected to use Levels 1 through 4 for STSPLUS; Level 5 is so coarse as to 
be almost useless. I have also written several utility programs to extract 
the map coordinate data from the original WDB files by level of detail and 
to build an index file for each level to speed access to the data. For the 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 13


orthographic projection, the data are also converted from latitude and 
longitude to geocentric Cartesian coordinates to minimize subsequent 
processing time. Although the resulting map database files are 
substantially smaller than the original data files, they are still quite 
large for the higher levels of detail; for example, the Level 1 files 
require approximately 1.5MB.
     STSPLUS attempts to select the map database files appropriate to a 
given magnification and map projection. If the selected level is not 
present, the program tries the next lower level until the selection process 
reaches Level 4, the lowest level of detail. The Level 4 map database files 
are required for operation of the program and are included in the standard 
program distribution. The Level 3 map database files are included with 
program registration and are available separately on my BBS. The Level 2 
and Level 1 map database files are available separately to registered 
users. See file README for registration information.
     Because of the size of the map database files, and because certain 
third party memory managers have had problems with the dynamic memory 
allocation (as implemented by Microsoft BASIC) used in STSPLUS prior to 
Version 9240, map data are ALWAYS read directly from disk. This means that 
map drawing times, even for the rectangular projection, are somewhat slower 
than with previous versions of STSPLUS. It also means that the program uses 
the disk files every time the map is redrawn. Users who plan on running 
STSPLUS for long periods of time may wish to place the map database files 
on a RAM disk to minimize wear and tear on their disk drive. Use Function 
Keys F7+F3 from the Main Menu to set up the correct map database path.
     The structure of the map database files is the same for all levels of 
detail and the index file (filetype .MCX) is the same size in each case. 
STSPLUS cannot distinguish between levels except by file names. Thus, if 
you are using a high speed computer such as a 486DX, you may rename the 
files to force STSPLUS to use a higher level of detail for a given zoom 
or magnification factor. All three files (.MCX, .MCP, and .XYZ) for a 
particular level must be kept together with the same filename or chaos will 
result! Naturally, drawing times will be increased as the price of the 
improved detail.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 14


PROGRAM SETUP AND USAGE NOTES
-----------------------------

     The following notes may prove helpful in setting up STSPLUS to operate 
most efficiently on your system or to provide hints in ways that some of 
the system and program features may be used to advantage.

DOS 5.0 CONFIG.SYS Setup
------------------------

     Users with DOS 5.0, especially those who take advantage of the high 
memory management capabilities and those who use add-on memory managers, 
should include the following line in their CONFIG.SYS file:

          STACKS=9,256

This command causes DOS to allocate more memory for the internal stacks 
used by DOS and some applications programs. DOS 5.0 seems more sensitive to 
the amount of allocated stack space than were prior DOS versions and 
programs which executed with no problems on DOS 3.3 may fail on DOS 5.0. A 
common symptom of insufficient internal stack space is that STSPLUS 
"freezes" the computer and a reboot is required. Other unpredictable errors 
can also result from stack errors. "9,256" creates 9 stacks of 256 bytes 
each; the "256" may be replaced by "384" or "512", and the "9" may be 
replaced by "15" if the basic STACKS command improves but does not cure the 
problems. See your DOS manual for additional information.
     The use of memory managers such as EMM386, QEMM386, and 386MAX with 
386 and 486 systems will cause the processor to operate in the Virtual 8086 
Mode, a "feature" which is not well documented by Microsoft. Users should 
be aware that this may cause considerable additional processor overhead, 
especially with graphics. For example, my 486DX/33 typically draws the 
orthographic map in almost half the time when a memory manager is NOT 
present but the improvement is less significant with a 386SX/20:

          486DX/33 Drawing Time WITHOUT 386MAX:       3.68 seconds
          486DX/33 Drawing Time WITH 386MAX:          6.70 seconds

          386SX/20 Drawing Time WITHOUT QEMM386:     17.91 seconds
          386SX/20 Drawing Time WITH QEMM386:        21.97 seconds

As the example times illustrate, the time saving is proportionally higher 
with a faster computer. Note, however, that a memory manager may be 
required for the use of extended or expanded memory and for certain 
applications. The use of different CONFIG.SYS files, selected by a batch 
file or other methods, can optimize performance for various applications. 
Another method is to boot the computer from a floppy disk (suitably 
formatted and configured) when the "simple" CONFIG.SYS is to be used.
     You can still use HIMEM.SYS and load DOS in high memory when EMM386 or 
another memory manager is not used by just including the following lines in
CONFIG.SYS:

          DEVICE=C:\DOS\HIMEM.SYS
          DOS=HIGH



Program STSORBIT PLUS Satellite Orbit Simulation                   Page 15


Using a RAM Disk
----------------

     A RAM disk is a simulated disk drive, created in the extended memory 
of your computer. Under most circumstances, it is much faster to read and 
write data to a RAM disk than to an ordinary disk drive. Remember that all 
data on a RAM disk is lost when the computer is shut down or power is lost. 
However, disk caching such as that provided by the Microsoft SMARTDRV 
driver or, better yet, hardware caching if it is included in your system, 
can perform as well as or even better than a RAM disk. Performance of disk 
caching varies as a function of both hardware and software, so testing may 
be required to determine the optimum configuration for a given computer.
     Because of program memory requirements, a RAM disk should be used only 
if your computer is equipped with expanded or extended memory. Using a RAM 
disk in conventional memory (the memory up to 640K) will use memory that 
STSPLUS (as well as most other programs) may need to operate correctly. The 
actual size RAM disk you can provide will depend upon how much memory is 
equipped in your computer and what memory may be required for other uses.
     The following line may be added to your CONFIG.SYS file and will 
create a 3000Kb RAM disk using the RAMDRIVE software provided with 
Microsoft DOS 5.0:

          DEVICE=G:\WINDOWS\RAMDRIVE.SYS 3000 /E

where the file "RAMDRIVE.SYS" is located in "G:\WINDOWS\" in this example. 
The "3000" specifies the size of the RAM disk in Kb, and the "/E" instructs 
the program to use EXTENDED memory. See your DOS manual for additional 
information.
     Many of the files used by STSPLUS are read only once when the program 
is first started. Little gain in performance will be achieved by putting 
these files on a RAM disk. The map database files (EARTH*.*) and the 
locations and features file (STSPLUS.LOC or whatever alternate filename(s) 
will be used) are read each time the map is drawn. If you frequently change 
satellites, moving the 2-line elements file(s) to a RAM disk may also 
improve performance. Users with fast hard drives and/or effective disk 
caching software will probably notice little or no difference in 
performance when using a RAM disk; however, if the program is being run for 
extended periods of time, using a RAM disk will eliminate hard disk use 
(and wear and tear) during program operation.
     All map database files MUST be in the MAP DATABASE path displayed when 
F7 is pressed from the Main Menu. The size of the RAM disk must be large 
enough to contain all map database files used for normal operation. Once 
the maximum map database level has been chosen, ALL lower level map 
database files must also be present in the directory. For the lower zoom 
factors, Levels 3 and 4 are sufficient; even when using the higher zoom 
factors, most users will be satisfied with Levels 2, 3, and 4. Map database 
file sizes are shown in the following table:

          EARTH1.MCP    613800 08-20-92   6:44a
          EARTH1.MCX     11914 08-20-92   6:44a
          EARTH1.XYZ    920700 08-20-92   6:44a
               3 files 1546414 bytes

          EARTH2.MCP    373948 08-06-92   1:32a
          EARTH2.MCX     11914 08-06-92   1:33a

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 16


          EARTH2.XYZ    560922 08-06-92   1:32a
               3 files  946784 bytes

          EARTH3.MCP     88144 08-06-92   1:04a
          EARTH3.MCX     11914 08-06-92   1:04a
          EARTH3.XYZ    132216 08-06-92   1:04a
               3 files  232274 bytes

          EARTH4.MCP     44804 08-06-92   1:07a
          EARTH4.MCX     11914 08-06-92   1:07a
          EARTH4.XYZ     67206 08-06-92   1:07a
               3 files  123924 bytes

     I use a batch file called "S.BAT", located in the same directory as 
STSPLUS.EXE, which takes care of copying the map database files to my RAM 
disk (drive J: in the example below) the first time the batch file is run 
and then starts STSPLUS:

          @echo off
          if exist j:\earth4.mcp goto Run
          copy /b \sop\earth4.* j:
          copy /b \sop\earth3.* j:
          copy /b \sop\earth2.* j:
          copy /b \sop\stsplus*.loc j:
          :Run
          stsplus /r %1

The files copied to the RAM disk in the example require somewhat less than 
1.5Mb. The line which begins "if exist ..." tests to see if the files have 
already been copied to the RAM disk and jumps to the label ":Run" if so. 
The "%1" allows me to enter an additional command line option (such as 
"/M" or "/EGA" for testing. Depending upon where the map database files are 
located, the drive and/or path will have to be changed in the lines which 
copy the files. I also set the various paths and filenames in STSPLUS using 
F7 from the Main Menu to those required for use with the RAM disk.


Copying Files for STSORBIT PLUS
-------------------------------

     STSPLUS is intended to be used on systems with a hard disk. If all 
files are present, up to 3MB may be required. While it is possible to 
operate the program from a high density floppy disk (with some files 
omitted), map drawing times are painfully and unacceptably slow.
     I recommend that a separate directory called STSPLUS be created for 
all of the required and optional files. If you received STSPLUS on disk 
with unpacked files, simply copy all files from the floppy disk(s) to your 
hard disk using the command:

          COPY /B A:*.* C:\STSPLUS

where the floppy drive is assumed to be A:, the hard disk is assumed to be 
C:, and the subdirectory STSPLUS already exists. Use the commands


Program STSORBIT PLUS Satellite Orbit Simulation                   Page 17


          C:
          CD \
          MD STSPLUS

to create the subdirectory STSPLUS if it does not already exist.
     If you received the program in compressed, self-extracting .EXE format 
(with a filename like SOP9338A.EXE and/or SOP9338B.EXE), create the STSPLUS 
directory as above then log into the STSPLUS directory and unpack the files 
with the commands:

          C:
          CD \STSPLUS
          A:SOP9338A

and repeat the last command for each .EXE file received, changing the 
command to reflect the correct filename.
     If you received the program in compressed format (.ZIP), copy the .ZIP 
file(s) to the STSPLUS directory and then enter the command:

          PKUNZIP <filename>

where <filename" is the name of the .ZIP file to unpack. After all files 
have been unpacked, you may delete the .ZIP files (but keep a backup copy 
just in case!). You MUST use PKUNZIP Version 1.1 or later to successfully 
unpack .ZIP files received from my BBS or from NASA SpaceLink BBS!

                           ********************
                           *  IMPORTANT NOTE  *
                           ********************

     If you are upgrading from a prior version of STSPLUS and 
     experience problems, delete the file STSPLUS.INI to force the 
     program to recreate its initialization parameters! This will 
     resolve most path and filename problems. Use Function Keys F7 and 
     F10+F3 from the Main Menu to set all program paths, filenames, 
     and options.


Slow Computers and 80x87 Math Coprocessor Chips
-----------------------------------------------

     STSPLUS has been designed for 80286/80287 or better computers equipped 
with an EGA or VGA color display. While the program can be executed on some 
older 8088 (XT-class) computers equipped with the 8087 math coprocessor, 
performance is seriously degraded. But it would seem that warnings and 
suggestions can NEVER convince people that their old clunker is past its 
prime or that the calculations required for orbital mechanics and graphics 
are very complex and tax even a powerful computer. The best mainframe 
computers we had a decade or more ago had trouble doing what I now take for 
granted on a personal computer!
     Not all personal computers are created equal. Further, the 80x87 math 
coprocessor chip can do many of the calculations ten or twenty times faster 
than the main processor. For 8088 (XT-class) and 80286 (AT-class) 
computers, this makes a tremendous difference AND for a very modest cost, 
often well under $100. Some users report problems with coprocessor chips 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 18


manufactured by IIT and USLI; while the problems may be related to the 
computer rather than the coprocessor chip, I recommend avoiding coprocessor 
chips by those manufacturers. Finally, I really don't want to hear from 
users how slow this program runs on older machines; I recommend the 
original STSORBIT if you want the best performance from any computer not 
equipped with a math coprocessor chip. Having said that, I DO run STSPLUS 
on my old 8MHz 8088/8087 LCD laptop with most features enabled.
     STSPLUS always runs as fast as the processor will permit and, since 
most features are available for all computer configurations, it is the 
responsibility of the user to select program features and options 
consistent with the desired performance. For example, the solar terminator 
requires considerable time to perform the required calculations and to 
update the display and, if this feature is not required, performace will be 
enhanced if it is disabled.
     As features have been added to STSPLUS, it has become increasingly 
difficult for very slow computers or computers not equipped with a math 
coprocessor to perform the necessary calculations in a reasonable time. 
STSPLUS tests to determine whether or not a math coprocessor chip is 
present and will use it if so. The following table illustrates the 
difference the processor and a math coprocessor chip make:

     Processor   Speed   Coprocessor   Time (secs)
     ---------------------------------------------
     486DX       33 MHz      YES               6.2
     386DX       20 MHz      YES              12.8
     386SX       20 MHZ      YES              16.8
     386SX       20 MHz       NO              66.0
     286          8 MHz      YES              30.0
     286         12 MHz       NO              86.6
     8088         8 MHz      YES              65.0
     8088         8 MHz       NO             426.4

The tests were performed with STSPLUS by measuring the time required from 
the Main Menu until the satellite appeared on the world map display using 
the rectangular map projection. All data were resident in memory (no disk 
operations required). All tests were made using the same display options 
(most were enabled). Slightly better performance can be achieved from the 
slower computers if some options, such as Sun terminator, are disabled. 
Clearly, the 8088 without the math coprocessor chip is not acceptable, and 
NONE of the computers without the math coprocessor chip performs very well.
     When STSPLUS begins, it checks to determine the type of processor and 
math coprocessor. If no math coprocessor chip is detected, the following 
caution message is displayed. Press ENTER (or any key) to continue.

                                  ** CAUTION **                           
                                                                          
              STSORBIT PLUS has detected NO MATH COPROCESSOR CHIP!           
                                                                          
                          CPU Type = 80386DX or 80387SX                   
                            NDP Type = (not installed)
                                                                          
      STSPLUS requires a Math Coprocessor Chip for acceptable performance.
                                                                          
        Calculation and map drawing times will be VERY SLOW. There is no  
         remedy except to add a Math Coprocessor Chip to your computer.   

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 19


                                                                          
                                                                          
                Users without a coprocessor should consider using         
                                                                          
                                    STSORBIT                              
                                                                          
               which is my original, simplified tracking program.         

     If, in spite of everything, you insist on using STSPLUS on your old 
clunker, here are a few cautions and reminders.

1.   Especially at startup and when drawing the maps, long time delays can 
     be expected with no math coprocessor -- on the order of minutes in 
     some cases. Status messages are presented on the screen during some 
     (but not all) of these delays. Note also that STSPLUS.EXE is 
     compressed to save disk space and is decompressed at load time; this 
     may cause a noticeable delay on some systems.

2.   Avoid using the orthographic projection with slow computers; the map 
     drawing times are much longer than the rectangular projections. Also 
     avoid high zoom factors since it is possible that the satellite may 
     move during the drawing process to the point where as soon as the 
     display is completed, it's time to redraw the map again. This process 
     will repeat endlessly and a reboot may be required. Restart the 
     program without the "/R" command line option and use F10+F6 from the 
     Main Menu to select WORLD or QUAD maps.

3.   If you have a monochrome monitor, experiment with the "/M" command 
     line option to force monochrome operation. On some monochrome systems 
     the program may otherwise fail with or without an error message. On 
     other monochrome systems, certain colors may not be visible when 
     simulated using shades of gray.

4.   The original CGA display, even when equipped with a color monitor, can 
     display reasonable graphics (640x320) ONLY in monochrome. Your color 
     CGA monitor buys you nothing for graphics that are quite inferior to 
     the EGA and VGA. 


Starting Program STSORBIT PLUS
------------------------------

     STSPLUS uses file STSPLUS.INI to save various information required for 
operation. Since the format of that file may change from time to time, 
STSPLUS ignores the file unless it was written by a recent program version. 
If the file does not exist, STSPLUS will automatically create it.
     To start program STSPLUS, use a batch file similar to "S.BAT" in the 
preceeding section or enter one of the following commands:

          STSPLUS            Automatic monitor, CGA/HGC/EGA/VGA

          STSPLUS /EGA       Force EGA (or lower) monitor

          STSPLUS /CLK       Use 43 or 60 lines for graphics display of
                             data and large clock characters. NOTE: This

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 20


                             feature available with EGA and VGA displays
                             ONLY! It is ignored for CGA/HGC monitors.

          STSPLUS /CGA       Force CGA monitor

          STSPLUS /M         Force monochrome operation, EGA/VGA

          STSPLUS /R         Resume last mission automatically

     Only one display option (/EGA or /CGA) may be used. Other options may 
be combined and entered in any order. For example, using the following 
command will resume the prior mission and force EGA mode:

          STSPLUS /R/EGA

     If you are using a Hercules Graphics Card, run the program MSHERC 
prior to running STSPLUS. This Microsoft program works with compiled BASIC 
programs to enable use of the Hercules Graphics Card. Orthographic 
projections are NOT supported for Hercules Graphics Cards. One user 
reported that setting the HGC to FULL and selecting Page Zero (using 
software supplied with the HGC) was sufficient for proper operation. At 
least one HGC "clone" user reported that STSPLUS could not be run under any 
circumstances.
     If you have already run STSPLUS and simply wish to resume the prior 
mission, use the /R (resume) command line option:

          STSPLUS /R

STSPLUS will sense the monitor type, enable color for EGA and VGA systems, 
then proceed directly to plotting the mission. The data from the last run, 
as saved in file STSPLUS.INI, is used to initialize the program. If 2-line 
elements were used, that file must also be present. Once started in this 
manner, pressing the ENTER key after the map is displayed will return to 
the Main Menu.


Predicting Visible Satellite Passes
-----------------------------------

     One of the most popular uses for a satellite tracking program is to 
show when a satellite of interest will be visible from a specified 
location. Using STSPLUS, my wife and I have spotted four different Space 
Shuttle missions, the Hubble Space Telescope, the Russian MIR Space 
Station, and many others with the naked eye. The trick, of course, is 
knowing when and where to look for the satellite.
     During normal operation, STSPLUS displays two timers in the form of 
countdown clocks (Minutes:Seconds), "AOS" and "LOS", for the user's 
location (as well as for a number of other events).  AOS, Acquisition of 
Signal, is the time remaining until the satellite is next within the circle 
of visibility. LOS, Loss of Signal, is the time remaining until the 
satellite next passes outside the circle of visibility. STSPLUS looks ahead 
four hours (240 minutes) from the time the map is drawn to determine the 
next AOS and LOS event; the clocks are blank if the time is greater than 
240 minutes. A quick inspection of these clocks can therefore determine if 
a potentially visible pass is upcoming within four hours.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 21


     Using its internal pass prediction feature, STSPLUS can look ahead 
in 48 hour blocks and list the passes when the selected satellite will 
be within the local circle of visibility (line of sight, no lighting 
constraints applied). 
     For more extensive tabular data on upcoming visible passes, external 
software must be used. There are a number of satellite tracking programs, 
most notably Paul Traufler's TRAKSAT and TS Kelso's TRAKSTAR, which can 
generate tabular data for a given satellite or group of satellites listing 
when the satellite(s) will be visible subject to various visibility 
constraints.


Predicting Satellite Passes with STSPLUS
----------------------------------------

     STSPLUS has a pass prediction capability (using F3 from the Main Menu) 
in addition to its graphics capabilities to make Line-of-Sight pass 
predictions for the current satellite quick and easy. Once a satellite has 
been selected (with F2 from the Main Menu), pressing F3 from the Main Menu, 
and selecting Data Format 9 (Pass Predictions ) will quickly produce a 
listing of the Line-of-Sight passes for that satellite over the next 48 
hour period. See the section "Pass Predictions and Data Output" for 
additional information. Here are some comments and suggestions for 
satellite viewing and tracking with STSPLUS.

1.   The pass predictions are listed in blocks of 48 hours beginning with 
     the current real or simulated time, and are given an arbitrary pass 
     number from 1 to 99. The data include the "AOS" or Acquisition of 
     Signal when the satellite rises above the local horizon, "MAX 
     VISIBILITY" or the time at which the satellite reaches the highest 
     altitude above the local horizon, "LOS" or Loss of Signal when the 
     satellite sets below the local horizon, and "Duration" or the total 
     time the satellite is above the local horizon. Note that "local 
     horizon" means the true horizon rather than local terrain. For either 
     visual or electronic tracking, the altitude above the local horizon 
     when the satellite may actually be tracked is usually at least five 
     degrees even under optimum conditions.

     CAUTION: Users with slow computers, especially those without a math 
     coprocessor, will find that pass predictions may require considerable 
     time -- up to tens of minutes using a slow 286 without a 287!

2.   Be sure to use current orbital elements for the satellite. My RPV 
     Astronomy BBS always has current 2-line orbital elements for some 650+ 
     satellites and these data are also available from other electronic 
     sources. For Low Earth Orbit satellites like the Space Shuttle or MIR, 
     orbital elements should be no more than about ten days old; for higher 
     orbit satellites, orbital elements remain accurate for longer periods, 
     up to about 30 days. Satellite maneuvers can radically change the 
     orbital elements. Pass predictions can be no more accurate than the 
     orbital elements used!

3.   Examine the "Alt" (maximum altitude) given under the "MAX VISIBILITY" 
     columns for each pass and select a suitable pass. As a general rule, 
     the higher the maximum altitude, the better the visibility. If you 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 22


     wish to see a particular pass as a ground track display, enter the 
     pass number and STSPLUS will set simulated time to about 30 seconds 
     prior to the time of maximum visibility and prepare the display. Press 
     "L" while the ground track is displayed to use the Location Map 
     centered on your location with the "bulls-eye" concentric circles of 
     equal altitude. You may stop/pause the display by pressing Function 
     Key F6, then move the satellite forward or backward in time using the 
     "+" and "-" keys and adjust the time step (1, 10, or 60 seconds) with 
     Function Key F4. Press ENTER to resume normal (simulated time) 
     operation.

4.   STSPLUS lists Line-of-Sight passes, those passes where the satellite 
     rises above the local true horizon, and all dates and times are given 
     in Coordinated Universal Time (UTC). Remember that under most 
     circumstances a "visible pass" means that the satellite is in full 
     sunlight and the viewer is in darkness. Although there are exceptions 
     in unusual situations, this generally restricts the times for visible 
     passes to the several hours prior to dawn and the several hours after 
     sunset. (Note, however, that "visible" to a ham radio operator or 
     radar tracking station simply means above the horizon!) In most cases, 
     the Space Shuttle and satellites such as MIR Space Station and Hubble 
     Space Telescope are visible with the naked eye given favorable 
     lighting and weather conditions. Satellites in higher altitude orbits 
     will be visible sooner before dawn and longer after sunset. Satellites 
     in very high orbits, no matter how large the satellite, are seldom 
     visible without high power binoculars or a telescope.

5.   The geometry of the pass and the attitude and geometry of the 
     spacecraft are also important. The relative angles between the Sun, 
     the satellite, and the viewer determine how light is reflected from 
     the surfaces of the spacecraft to you, the viewer. A spacecraft 
     passing between you and the Sun may not reflect much light to you and 
     may therefore not be visible even at higher altitudes. On the other 
     hand, a spacecraft nearer the horizon but on the other side of you 
     from the Sun may appear brilliantly lighted. The kinds of surfaces on 
     the spacecraft are important too; solar panels and flat surfaces can 
     reflect enough light to appear the most brilliant objects in the sky 
     while larger but rounded spacecraft may seem all but invisible.

6.   Given otherwise good conditions and favorable weather, the single most 
     important factor is spacecraft apparent altitude ("Alt") during a 
     pass. This is the spacecraft's apparent elevation above your local 
     horizion. Depending upon local conditions, an altitude of at least 5 
     to 10 degrees will generally be necessary before a spacecraft can be 
     seen even under the best lighting conditions. In the Los Angeles area, 
     at least 20 or 30 degrees is a better number to use because of smog, 
     haze and light polution (except when looking out over the Pacific 
     Ocean).

7.   After altitude, the azimuth ("Azm") is the number which describes the 
     direction from the viewer to the spacecraft at any moment. This is 
     given in the sense NESW, North to East to South to West, in degrees. 
     For a good pass after sunset, for example, an azimuth ranging from 60 
     to 150 degrees would indicate a pass moving generally from the 
     Northeast to the Southeast, ideal lighting conditions with the Sun in 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 23


     the West.

8.   Remember that STSPLUS automatically sets SIMULATED TIME when using the 
     pass prediction feature to display passes. If simulated time is 
     already in effect, pass predictions start from the current simulated 
     time and a new simulated time is automatically set for a selected 
     pass. Once set, simulated time remains in effect until changed by 
     selecting another pass or until reset with F8 from the Main Menu. To 
     return to "real time", press F8+F1 from the Main Menu. The Main Menu 
     displays the current time with the time mode in effect labeled as 
     "Current Time" or "Simulated Time".


Predicting Satellite Passes with TRAKSTAR
-----------------------------------------

     In order to generate detailed tabular predictions for satellite 
passes, an external program is required. I recommend two programs for this 
purpose: Paul Traufler's TRAKSAT and TS Kelso's TRAKSTAR. Each programs is 
copyrighted by the respective author and is readily available. They are 
both fine programs and set a standard against which other satellite 
tracking programs are measured for performance and accuracy.
     I have selected TRAKSTAR as the default external program used with 
STSPLUS for two reasons: first, the program quickly produces very accurate 
tabular data without graphics; and second, TRAKSTAR requires minimum memory 
and is easily configured for seamless operation with STSPLUS.
     TRAKSAT is a very large program with many features, and most computers 
will not have sufficient memory to execute TRAKSAT when STSPLUS "shells" to 
DOS. In order to run TRAKSAT, users must first exit STSPLUS (press "ESC" 
from the Main Menu).
     For additional information on these programs, contact the authors:

          TRAKSTAR:      Dr. T. S. Kelso
                         2340 Raider Drive
                         Fairborn, OH  45324-2001  USA

                         BBS: Celestial BBS
                              (513) 427-0674
                              300/1200/2400/4800/9600 baud

          TRAKSAT:       Paul Traufler
                         111 Emerald Drive
                         Harvest, AL  35749  USA

                         BBS: RPV Astronomy BBS
                              (310) 541-7299
                              2400/9600/14400 baud

                              RPV Hotline BBS
                              (310) 544-8977
                              1200/2400 baud

As a courtesy to the author, I suggest enclosing a stamped, self-addressed 
envelope if you write and request a reply. The current version of each 
program is always posted on the indicated BBS and messages may be left 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 24


there for the author.
     There is no "standard" filetype used for 2-line elements files; 
typical filetypes in regular use are ".TXT", ".TLE", ".N2L", and ".ELE"; 
some files also include comment lines, multi-line commentary, or additional 
data, some or all of which must be removed prior to use with most satellite 
tracking programs. As released by Dr. Kelso, TRAKSTAR expects a filetype of 
".TLE" and cannot accept any other filetype without being re-compiled. 
STSPLUS defaults to both filetype ".TXT" and ".TLE". TRAKSAT defaults to 
filetype ".TXT" only. However, 2-line elements files, even on Dr. Kelso's 
Celestial BBS, may use either ".TLE" or ".TXT", depending upon the file. 
For the past four or five years, Paul Traufler and I have been jointly 
releasing file TLEnnn.TXT (usually as file TLEnnn.ZIP, where "nnn" is a 
number like "143"). Until February, 1993, the file was named NASAnnn.TXT. 
This file is a sorted concantenation of files TLE.TXT and GROUP000.TLE from 
Celestial BBS and currently includes 2-line elements for some 700+ 
satellites.
     STSPLUS solves the filetype problem with TRAKSTAR by dynamically 
creating a file called STSPLUS.TLE which contains the 2-line elements for 
the currently selected satellite. Since STSPLUS can select 2-line elements 
from a file of any size, calling TRAKSTAR through STSPLUS also circumvents 
a minor problem in the current version of TRAKSTAR which limits the number 
of satellites in a 2-line elements file to 250 element sets. As a 
convenience, STSPLUS also dynamically creates the files STSPLUS.OBS (which 
contains the name, coordinates, and elevation of the current user location) 
and TRAKSTAR.CFG (which contains the drive and path information for 
TRAKSTAR).
     An accurate elevation (above mean sea level) for the user location is 
required for accurate calculations in any satellite tracking program, 
including STSPLUS, TRAKSTAR, and TRAKSAT. Note that the elevations of most 
locations in file STSPLUS.CTY are not readily available and have been set 
to zero. The elevation is the last parameter on each line in file 
STSPLUS.CTY and is given in integer meters; 1 meter equals 3.28083 feet.
     STSPLUS is coded to operate with TRAKSTAR Version 2.15. It may or may 
not operate correctly with other versions. To set up program TRAKSTAR 
either for independent use or for use with STSPLUS, follow the following 
steps:

1.   Copy the TRAKSTAR files to your hard disk. Unpack the files if they 
     are contained in an archive file such as TRAKSTR2.ZIP. I recommend 
     using a separate directory called "TRAKSTAR". The complete TRAKSTAR 
     package includes documentation, Pascal source, example and test files, 
     and the program itself. The following two files are required for 
     operation with STSPLUS:

          TRAKSTAR.EXE        Main Program
          TRAKSTAR.HDR        Header File

     Additional files are required for independent operation. Read the 
     TRAKSTAR documentation for details.

2.   Run STSPLUS and enter the drive and path information for TRAKSTAR by 
     pressing F7+F5 (Set FILENAMES and PATHS) from the Main Menu. STSPLUS 
     will automatically default to its own drive and directory if you omit 
     this step.


Program STSORBIT PLUS Satellite Orbit Simulation                   Page 25


3.   Select the desired 2-line elements file and satellite by pressing F2 
     from the Main Menu.

4.   When the map is on the screen and you have verified that the correct 
     satellite is being tracked, press ENTER to return to the Main Menu.

5.   Now press F4 from the Main Menu to run TRAKSTAR. You should 
     immediately see TRAKSTAR's opening screen and the first selection. 
     Make the various selections by using the up and down arrow keys to 
     move between selections and press ENTER when you have the correct 
     selection. Don't forget to press SPACE to select the satellite!

                               *************
                               *  CAUTION  *
                               *************

     TRAKSTAR Version 2.15 uses the DOS clock to determine the default 
     start and stop times for its calculations. Not mentioned in the 
     TRAKSTAR documentation, however, is the fact that TRAKSTAR assumes 
     that the computer is set to Coordinated Universal Time (UTC). Be sure 
     to take that difference, including the date, into account when 
     entering start and stop times!

6.   TRAKSTAR will now make its calculations and write the results to a 
     file. The file is written in the TRAKSTAR directory and will overwrite 
     an existing file of the same name. The time required will be a 
     function of the time span and time interval requested as well as the 
     calculation speed of your computer. Read the TRAKSTAR documentation 
     carefully so that you will recognize the name of the file that 
     TRAKSTAR writes. For example, requesting visible passes for the Hubble 
     Space Telescope (NORAD #20830) will result in a filename of "VOB20830" 
     and a filetype which is the last three digits of the element set 
     number (such as ".866").

7.   As soon as TRAKSTAR finishes, you will return to STSPLUS's Main Menu 
     and may continue normal operations.

8.   To examine the tabular data produced by TRAKSTAR, you must either 
     "shell to DOS" using F9 from the Main Menu or exit STSPLUS by pressing 
     ESC at the Main Menu. Use an ASCII editor to view the file or send it 
     to your printer for hard copy.

If STSPLUS cannot find TRAKSTAR.EXE (or TRAKSTAR.BAT, see below) in the 
selected directory, an error message will be displayed. Press ENTER to 
return to the Main Menu.
     An alternative method is to create a file TRAKSTAR.BAT in which you 
place all commands required to run TRAKSTAR or the satellite tracking 
program of your choice. STSPLUS.TLE and TRAKSTAR.CFG will still be written 
to the selected directory but they need not be used. This method is only 
recommended for individuals who understand the use and operation of DOS 
batch files. 



Program STSORBIT PLUS Satellite Orbit Simulation                   Page 26


Printing Graphics Screens
-------------------------

     Many users have requested that I add a "print" function to STSPLUS. 
Given the number and variety of printers available for use with these 
systems and the fact that I only have a couple of printers I can use for 
testing, this is not practical within STSPLUS. However, DOS includes the 
GRAPHICS command which may be used with many computers to enable printing 
of graphics images. Check your DOS and printer manuals for details. As an 
example, I use the following command on systems equipped with a Hewlett-
Packard LaserJet II or III:

          GRAPHICS LASERJETII

     There are also quite a number of screen capture and print screen 
programs, both commercial and shareware, which can perform this task. Note, 
however, that all these programs are TSR's (Terminate and Stay Resident) 
and some could interfere with STSPLUS's operation.
     Some print screen programs, inculding DOS's built-in GRAPHICS command, 
do not render colors very well. Certain colors may not be visible on the 
printed copy at all. For such programs, use the "/M" command line option to 
force monochrome operation when you wish to print graphics images from the 
screen.


Known STSPLUS Problems and Bugs
-------------------------------

     STSPLUS is being used on thousands of computers around the world 
without any significant problems. However, like almost any computer program 
and in spite of my best efforts, there are several known problems or "bugs" 
with STSPLUS. Some are the result of slow computers, others are in the 
program itself. Hopefully, some or all of these problems, those I can 
reproduce at least, will be repaired in due course. Some problems are 
caused by other software interfering with the program's operation. Still 
other problems are the result of incompatible "IBM-compatible" computers 
for which there is no remedy.
     One "problem" which I frequently hear about is that the user's CGA 
color monitor only displays STSPLUS in monochrome. THIS IS NOT A BUG! CGA 
systems display "high resolution" 640 x 200 graphics in monochrome ONLY. 
Compared to the EGA or VGA, that resolution is barely acceptable. The color 
graphics mode for the CGA is 320 x 200 which is inadequate for STSPLUS.

1.   STSORBIT PLUS has been run extensively on systems using Microsoft DOS 
     3.3 and 5.0 and there are no known problems with those operating 
     systems EXCEPT the STACKS problem with DOS 5.0 (see the section 
     Program Setup and Usage Notes above). Because of the many bugs 
     reported, I do NOT recommend use of DOS 4.xx under any circumstances; 
     upgrade ASAP to DOS 5.0! Users report memory allocation problems with 
     some earlier versions of Digital Research DRDOS 6.0 and certain third 
     party memory allocation programs. A typical symptom of this kind of 
     problem is that you cannot return to DOS without either an error 
     message or the computer freezing.

2.   Note that not all computers (especially older CGA systems) will 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 27


     display the extended graphics characters used for the large clock 
     characters (selected with F2 when the map is displayed). The symptom 
     of this problem is that the lower left portion of the data block is 
     mostly blank after pressing F2. If you have this problem and your 
     computer is running DOS 3.x or DOS 5.0, enter the command "GRAFTABL" 
     at the DOS prompt before running STSPLUS or include the line 
     "GRAFTABL" in your AUTOEXEC.BAT file; this sets the "code page" to 
     enable the computer to display the extended graphics characters. [The 
     program GRAFTABL.COM is included as part of DOS in most cases.]

3.   Some users report problems with certain Terminate and Stay Resident 
     (TSR) programs for which the only remedy is to remove the offending 
     TSR. This usually requires a "trial and error" approach to pinpoint 
     the TSR causing the problem. The best method is to remove ALL such 
     programs from your AUTOEXEC.BAT file, including the DOS 5 "DOSSHELL",
     to make sure the program will work with your computer. Similarly, 
     delete all special memory and device drivers from your CONFIG.SYS 
     file. For DOS 5.0, add the line "STACKS=9,256" to your CONFIG.SYS 
     file. In some cases it may be necessary to increase the number 256 to 
     384 or 512. One user reported a problem on an IBM PS/2 when a mouse 
     driver was used (but I regularly execute STSPLUS on different 
     computers with my mouse active!).

4.   Several users have reported occasional "BASIC Error 11" problems; 
     BASIC reports this error as "Division by Zero". The only way I have 
     been able to reproduce this error is to restart the program using the 
     command line "STSPLUS /R" after I have deleted the 2-line file used on 
     the prior run; to avoid this error, do not use the "/R" command line 
     option and select a new 2-line file using F2. This error may also be 
     the result of a memory limitation (with multitasking enabled?) or it 
     may be a BIOS problem associated with a specific computer. 

5.   All VGA adapter cards are not equal, in case any of you had some 
     illusions left. In at least one case, the aspect ratio of the display 
     is incorrect when the display is operated in the EGA simulation mode. 
     The vertical scale is compressed by about 20% as compared to either a 
     true EGA display or other (correct) VGA displays. So far as I know, 
     there is no remedy. Early VGA cards (the 449 card from Zenith is an 
     example) are not always recognized as VGA; the card is not register 
     compatible with the IBM standard and is recognized as EGA instead.

6.   There appears to be a subtle problem when changing to or from Daylight 
     Savings Time (which recently happened and "announced" the bug). The 
     display appears to get caught in a loop, endlessly redrawing the 
     screen or shows the wrong time and/or time zone. To avoid the problem, 
     change the Daylight Flag then EXIT THE PROGRAM AND RESTART.

7.   Not all computers (especially older CGA systems) will display the 
     extended graphics characters used for the large clock characters. The 
     symptom of this problem is that the lower left portion of the data 
     block is mostly blank after pressing F2. If you have this problem and 
     your computer is running DOS 3.x or DOS 5.0, enter the command 
     "GRAFTABL" at the DOS prompt before running STSPLUS or include the 
     line "GRAFTABL" in your AUTOEXEC.BAT file; this sets the "code page" 
     to enable the computer to display the extended graphics characters. 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 28


     [The program GRAFTABL.COM is included as part of DOS in most cases.]

8.   Some math coprocessor chips have caused problems. In at least two 
     reported cases, early version 386SX math coprocessor chips from IIT 
     did not execute correctly and generated random errors; ITT replaced 
     the suspect chips and the problems disappeared. On a 40MHz 386SX 
     system, a USLI 387SX chip did not operate correctly; a Cyrix 387SX 
     chip cured the problem. No problems have been reported for Intel or 
     Cyrix chips.

9.   Finally, as noted elsewhere, all computers are NOT equal. There are 
     some computers which will not execute STSPLUS under any circumstances. 
     Tandy is the most common offender followed by Leading Edge. Some 
     models from these manufacturers have BIOS problems or errors which 
     prevent programs compiled with the Microsoft BASIC compilers from 
     operating (sometimes only in graphics modes). There is no remedy. 
     Other computers, Ergo for example, exhibit "strange" behavior in some 
     graphics and text modes. There is sometimes an update or workaround 
     for these problems; check with the manufacturer.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 29


Preparing 2-Line Elements using VEC2TLE by Ken Ernandes
-------------------------------------------------------

     Especially for Space Shuttle missions, Earth-centered inertial ("ECI") 
cartesian state vectors may be the only orbital information available in 
near real time. Such a state vector, consisting of position and velocity 
data at a specified time, is sufficient to determine the instantaneous 
orbit of a satellite. NASA and other agencies may provide state vectors 
referenced to the mean equator and equinox of the Besselian year 1950 
("M50", "Mean of 1950", or "B1950") with units of measure in feet and feet 
per second. Data may also be available for the true equator and equinox of 
date (such as the state vectors generated by STSPLUS), the mean equator and 
equinox of the Julian year 2000 ("J2000"), or in the time-independent 
Earth-fixed Greenwich ("EFG") coordinate systems. Kilometers or nautical 
miles may also be used as the units of measure.
     However, STSPLUS and most other satellite tracking programs require 
orbital data in the "2-Line Elements" or "TLE" format and state vectors 
must be converted to that format before the data may be used. The 2-Line 
format originated as 2-Card Elements back in the days of IBM punched cards 
at NORAD (North American Aerospace Defense Command, now US Space Command), 
and has become the de facto standard format for orbital data used with 
satellite tracking software.
     Mr. Kenneth J. Ernandes has written program VEC2TLE, Vector to Two 
Line Elements, specifically to convert state vectors to the 2-line format. 
VEC2TLE is copyrighted software distributed as shareware, and registration 
is required prior to regular use. Mr. Ernandes has extensive experience in 
orbital mechanics with US Space Command (formerly NORAD) and in industry, 
and has used his expertise to create a precision conversion program. For 
additional information and registration details, write:

          Mr. Kenneth J. Ernandes
          16 Freshman Lane
          Stony Brook, NY  11790-2712

          CompuServe:  70511,3107
          Internet:    70511.3107@cis.com

When writing Mr. Ernandes for information, I suggest including a stamped 
self-addressed envelope as a courtesy. The current version of VEC2TLE is 
usually posted on the RPV ASTRONNOMY BBS and on the CompuServe Astronomy 
and Space Forum.
     Note that although 2-line elements can be generated using only the 
data in an ECI state vector and these elements will yield an accurate 
position at the specified time, the "epoch" of the data, additional data 
(in particular, Drag and B-Star parameters) are required to generate 2-line 
elements which propagate accurately over time. Certain additional 
parameters, such as element set number and orbit number, do NOT affect the 
accuracy of the propagated position; these data may be obtained from other 
sources or default values may be used. US Space Command assigns a Catalog 
Number, often referred to as the "NORAD Number", some time after launch; 
pre-launch elements for Space Shuttle missions may have a temporary Catalog
Number (corresponding to the mission number) until the actual Catalog 
Number is assigned. The IAU Designation is assigned by the International 
Astronomical Union at the time a launch is registered by the launching 
country and may be blank. Element set ("ElSet") numbers are assigned 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 30


arbitrarily by the originating individual or agency and have no effect on 
the orbital data. Orbit (or revolution or "REV") numbers are incremented on 
each revolution at the ascending node, the point at which a orbit crosses 
the equator heading North. Note that US Space Command does not usually use 
the same reference for orbit numbers as does NASA; NASA defines the first 
partial orbit as "Rev 1" whereas US Space Command may call that "Rev 0" or 
some other arbitrary number. At least for Space Shuttle missions, it is 
common practice to adjust USSPACECOM orbit numbers to conform to the NASA 
convention.
     VEC2TLE accepts all data required to form a complete 2-line orbital 
element set, either as manually entered data or from a properly formatted 
file, performs limited error checking on these data, then displays and 
writes the generated 2-line elements file. The initial public release of 
VEC2TLE, Version 9319, supports STSPLUS Data Mode 5 through 7 state vector 
formats. The program also supports a variety of coordinate systems, units 
of measure, and time formats.
     Care must be taken when using VEC2TLE that the proper units of measure 
(kilometers, feet, or nautical miles), coordinate system (ECI or EFG), and 
epoch (True of Date, Mean of 1950, etc.) are used. See the VEC2TLE 
documentation for additional information on the available options. STSPLUS 
generates ECI X-Y-Z state vectors for the true equator and equinox of date 
and may use any of three units of measure. NASA, on the other hand, 
generates their state vectors for the mean equinox and equator of 1950 
("M50") and uses feet and feet/second units of measure. Obviously, using 
the wrong units of measure or coordinate system will yield invalid results!
     VEC2TLE has been validated and tested in conjunction with STSPLUS 
using NASA ECI state vectors (provided courtesy Willie Musty, Mission 
Support, Rockwell International, Downey, CA) during Space Shuttle missions 
STS-56 and STS-55 in early 1993. The resulting 2-line elements yielded 
orbiter positions which corresponded exactly with those shown live on NASA 
Select TV, and the 2-line elements were in close agreement with 2-line 
elements subsequently released by US Space Command for a comparable epoch. 
In fact, during mission STS-56, Rockwell used 2-line elements at their 
Mission Control Center which I generated using VEC2TLE when USSPACECOM and 
NASA 2-line elements were not forthcoming in a timely manner.
     In addition to simply converting state vectors to 2-line elements, 
the primary purpose of the program, VEC2TLE may be used in conjunction with 
STSPLUS or other sources of state vectors to model orbit adjust burns and 
similar maneuvers. STSPLUS is used to generate a state vector at the 
midpoint of the burn, the appropriate delta velocities (obtained 
independently) are added to the state vector quantities Xdot, Ydot, and 
Zdot, then new, post-burn 2-line elements are generated with VEC2TLE. More 
complex maneuvers may also be calculated or modeled although these more 
complicated exercises are not recommended for the novice. VEC2TLE may also 
be used to precess a set of 2-line elements to the prior Ascending Node, 
required by some software. See the VEC2TLE documentation for additional 
discussion and references.
     My thanks to Ken Ernandes for writing VEC2TLE, for making it available 
to the satellite tracking community, and for his assistance in validating 
the precision state vector output data from STSPLUS. Thanks also to Willie 
Musty (for providing state vectors) and to Joel Runes (for validation and 
testing). As with any complex program, considerable effort has been 
expended in writing, testing, and documenting the program. If you use 
VEC2TLE, please register your copy so as to encourage Ken and others to 
continue writing such useful software.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 31


PROGRAM OPERATION
-----------------

     STSPLUS automatically checks for the presence of a VGA or EGA and will 
execute in color if one is found UNLESS the /M command line option is used 
to force monochrome operation. However, if you wish to operate STSPLUS in 
the EGA mode when you have a VGA monitor, you must use the /EGA option. In 
cases where a monochrome monitor is connected to an adapter which simulates 
color with gray scale, the /M command line option may be omitted but the 
various portions of the display may or may not be visible. STSPLUS depends 
upon the Microsoft BASIC Compiler to determine whether or not a particular 
monitor type is available. Some video adapter boards which claim to be VGA 
are not recognized as such by BASIC and therefore cannot be used in the 
higher resolution VGA display mode. Similarly, "clone" Hercules Graphics 
Cards do not always perform correctly.
     The /M option is not required for HGC and CGA graphics operation, 
since those adapters always render their "high resolution" graphics in 
monochrome. Although color CGA systems do have a 3-color mode, the limited 
number of colors and coarse resolution of 320x200 is not suitable for 
STSPLUS. Naturally, the appearance of the program is enhanced by the use of 
color. The vertical resolution is also adjusted depending upon the type of 
adapter which has been detected. Microsoft does not support SVGA adapter 
cards, unfortunately. Once STSPLUS has started, the display type may not be 
changed without exiting the program at the Main Menu with the ESC key, then 
restarting the program with the desired command line options.
     The program checks for the presence of a math coprocessor and will use 
it if found. Since the calculations required to determine orbital data are 
very complex, the use of a math coprocessor will improve the speed of 
operation by a very substantial amount.
     STSPLUS selects the icon or symbol used to graphically represent the 
satellite based upon the satellite name. Names which start with the letters 
"STS" will use an icon resembling a plan view of the space shuttle and all 
other missions will use an icon resembling the Hubble Space Telescope.
     STSPLUS reads the map coordinates from the appropriate map database 
files. These coordinates are converted to screen coordinates for the type 
of monitor detected, the current projection method, and the current 
magnification or zoom factor.
     Once the initial "housekeeping" chores have been performed, the Title 
Screen is displayed for 15 seconds for normal program operation or for 3 
seconds if the /R command line option has been used. The Main Menu, 
described in a subsequent section, is then displayed. Press ENTER to 
proceed to the Main Menu immediately.


Program STSORBIT PLUS Satellite Orbit Simulation                   Page 32


                              Program STSORBIT PLUS

                  Space Shuttle and Satellite Orbit Simulation
                                  Version 9338

                        RighTime Version 2.53 detected!

                   Current time:  15:02:17 PST   23:02:17 UTC
                   Current date:    02/28/1993     02/28/1993


                      Last Mission = Hubble Space Telescope
                    2-Line Elements File = F:\TLE\TLE147.TXT

                          CPU Type = 80386DX or 80387SX
                          NDP Type = 80387DX or 80387SX
                              Display = VGA Color

                  (C) Copyright David H. Ransom, Jr., 1989-1993
                              All rights reserved.

     The Title Screen displays the program version, current time and date, 
last mission, and 2-line elements path and filename. It also displays the 
type of Central Processing Unit (CPU) and Numeric Data Processor (NDP, or 
math coprocessor), and the type of display. The program detects 8088, 
80286, 80386, and 80486 processors and the associated math coprocessor; if 
the math coprocessor is not present or fails a simple test, it will show as 
"(not installed)". The program detects CGA, HGC, EGA and VGA display 
systems; unless the "/M" command line option is used to force monochrome 
operation, EGA and VGA systems will always indicate "Color".
     STSPLUS is now "aware" of program RighTime by Tom Becker. If RighTime 
is active, the current version number will be displayed; if RighTime is not 
active or is not detected, no message will be displayed. STSPLUS is 
configured to use RighTime Version 2.5+; performance with prior versions 
may be unpredictable and audible alarms should NOT be enabled in that case. 
See the section "Accurate Time and the Personal Computer" for a further 
discussion of RighTime and other aspects of maintaining accurate DOS time.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 33


STSORBIT PLUS SATELLITE TRACKING FEATURES
-----------------------------------------

     The principal objective of STSPLUS is to graphically display the 
position of the space shuttle or satellite relative to a map of the world 
or some relevant portion of the world along with relevant time and 
numerical data. Two map projections and six different map displays are 
available: Orthographic, World, Quadrant, Zoom, Location, Tracking Station, 
and Satellite Motion. Varying magnifications or zoom factors are available 
in most map modes. Each is discussed below.
     In addition to the map itself, a number of other items of interest are 
displayed. Some features are available only with higher resolution displays 
(EGA and VGA) in order to avoid cluttering the display screen. Other 
features may be enabled or disabled according to the user's preference. The 
sections which follow the map types discuss these various features.


Orthographic Projection Maps
----------------------------

     The orthographic projection views the Earth as a sphere as if from a 
great distance (perspective is not included) and is the latest addition to 
the map projections available in STSPLUS. This projection has the advantage 
that the map may be centered at any point on the Earth and may include a 
pole, especially helpful for high inclination satellite orbits. Unlike the 
world map shown with rectangular projection, only one hemisphere can be 
seen at a given time and therefore automatic map redrawing is always 
enabled. Because of the more complex calculations required to generate a 
map, users with slower computers may find that drawing times in the 
orthographic modes are unacceptably long. (A math coprocessor will improve 
map drawing times by almost a factor of ten!)
     Orbital ground tracks, especially for high inclination orbits, and the 
solar terminator are more readily understood using this projection. The 
orthographic projection displays circles of visibility as true circles near 
the center of the map. 
     The default magnification for orthographic maps is 100% which displays 
the entire globe as a hemisphere. Using the PgUp and PgDn keys, the 
magnification may be selected from 100% to 4000% (2000% if Level 1 maps are 
not present). Each time the map is drawn, the center of the map is selected 
so that the satellite will remain on the map for the longest time 
practical. When high magnification factors are selected and the computer is 
not equipped with a math coprocessor, it is possible that the map drawing 
time will exceed the time the satellite is in view; this will cause the map 
to be immediately redrawn. The current map database file and map drawing 
time are shown near the bottom of the data block (e.g. "EARTH4   10.91").
     Because only one hemisphere is shown (or a portion of a hemisphere 
when magnification factors greater than 100% are used), automatic map 
generation is ALWAYS enabled in orthographic modes. In addition, even if 
the satellite never leaves the current map (as is the case with 
geosynchronous satellites), the map will be redrawn every 2.5 hours. Users 
without a math coprocessor may find that map drawing times in orthographic 
modes are painfully slow. The only remedy is to purchase a new, more 
powerful computer or to add a math coprocessor chip; this will improve 
performance by about a factor of ten and the math coprocessor chips are now 
relatively inexpensive, often under $100.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 34


     The orthographic version of the Satellite Motion Map, enabled with the 
"M" key when the map is displayed on the screen (EGA and VGA systems ONLY) 
centers the satellite on the map and "moves" the map beneath the satellite 
using EGA graphics. The next map is started in offscreen memory as soon as 
a map is completed and displayed, then that map is displayed when completed 
and the process is repeated. Especially for slower computers, this map mode 
may be preferred since a map is always on the screen regardless of the 
drawing time required.
     As a footnote, the orthographic version of the Satellite Motion Map 
can duplicate many of the views presented on NASA Select TV during a 
mission. NASA frequently uses the equivalent of MAG=150 or MAG=200 for 
their display. STSPLUS, however, can display far greater map detail than 
can the NASA program, especially when the Level 3 and Level 2 map database 
files are present.


Rectangular Projection World Maps
---------------------------------

     The STSPLUS rectangular projection (similar to Mercator projection) 
ground track display defaults to a map of the world centered on the Prime 
Meridian (0 degrees) and extending from approximately +85 degrees North 
latitude to -85 degrees South latitude using a linear cylindrical 
projection. Omitting the two 5 degree bands at the poles permits better 
detail in the mid latitudes where all space shuttle orbits and many other 
satellite orbits are concentrated and avoids the extreme distortion 
inherent in the rectangular projection near the poles. Ground track details 
very near the poles are therefore sacrificed for a better display in the 
main portion of typical orbits. The vertical resolution of the display is 
automatically adjusted for the type of display system in use from 200 lines 
(CGA) to 480 lines (VGA). Two World Maps are available: one centered on the 
Prime Meridian at Greenwich, England (0 degrees longitude); and, one 
centered on the International Date Line (180 degrees longitude).
     All screen maps drawn by STSPLUS use a vector database derived from 
the Micro World Database II. The full map of the world as used here 
can include up to approximately 470,000 sets of vector coordinates 
describing the world's coastlines, islands, lakes, and major rivers when 
used with the highest detail (Level 1) map database.
     Pressing the "W" or "0" key will switch the display to the World map. 
If automatic map generation is enabled, STSPLUS will select the map which 
most nearly centers the satellite on the map. If automatic map generation 
is disabled, pressing "W" or "0" will toggle between the two maps. When 
automatic map generation is enabled, the letter "A" appears in the upper 
right of the screen.


Rectangular Projection Quadrant Maps
------------------------------------

     The original STSORBIT program used a digitized pixel map of the world 
derived from an EGA display. As a consequence of the EGA source, boundaries 
were sometimes discontinuous on VGA displays and the display on a CGA was 
sometimes difficult to read. STSPLUS uses a vector map drawing method which 
automatically adjusts to the display type and the scale of the map. The full 
world map (above) is quite similar in appearance to the original display.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 35


     However, some geographic details are still difficult to distinguish, 
even on a VGA display. STSPLUS includes twelve quadrant maps, each overing 
1/4 of the Earth's surface and using rectangular projection. These are 
numbered 1 to 12 and are centered on the world map roughly according to the 
following illustrations:
                   0                                180             
     +---------------------------+     +---------------------------+
     |             |             |     |             |             |
     |    1        4        7    |     |    7        10       1    |
     |             |             |     |             |             |
     |             |             |     |             |             |
     |             |             |     |             |             |
     |    2        5        8    |     |    8        11       2    |
     |             |             |     |             |             |
     |             |             |     |             |             |
     |             |             |     |             |             |
     |    3        6        9    |     |    9        12       3    |
     |             |             |     |             |             |
     +---------------------------+     +---------------------------+


The center vertical quadrants in the left illustration, 4 through 6, are 
centered on the Prime Meridian at zero degrees longitude (Greenwich, 
England). The center vertical quadrants in the right illustration, 10 
through 12, are centered on the International Date Line at 180/-180 
degrees. The center horizontal quadrants, 2, 5, 8, and 11, are centered on 
the Equator.
     Each individual quadrant map may be selected by pressing the 
corresponding number key, "1" through "9"; use keys "!", "@", and "#" to 
select quadrants 10, 11, and 12 respectively. Pressing any of these keys 
for individual quadrant maps will disable automatic map generation if it is 
enabled (indicated by the letter "A" at the upper right of the screen). 
Pressing "Q" will allow STSPLUS to select the quadrant most appropriate for 
the satellite's current position.


Rectangular Projection Zoom Maps
--------------------------------

     Although I was pleased with the enhanced maps using the Quadrant Mode, 
the map data base files contain far more information than can be 
effectively displayed in that mode. The next obvious step was to add the 
ZOOM feature, maps which yielded greater detail and which spanned as little 
as 30 degrees across the screen, six times better than the 180 degree 
quadrant maps. This approaches the practical limit for the map database 
files. Because of the smaller area covered, a different approach was used 
for map selection. There would simply be too many different possibilities 
for manual selection so a fully automatic Zoom Mode was implemented which 
calculates the optimum map center point based upon the current position of 
the satellite.
     Press the "Z" key to enable Zoom Mode. The initial map width is 75 
degrees; use PgUp to widen the map width (up to 180 degrees) or PgDn to 
narrow the map width (down to 30 degrees. The Home key will always select 
75 degrees width and the End key will return to the prior field of view. 
The width of the map is shown at the upper left of the map display. Press 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 36


the TAB key to enable or disable automatic map generation (the map will 
always be redrawn). When automatic map generation is enabled, the letter 
"A" appears in the upper right corner of the screen next to the map width 
or field of view. Zoom field of view selections are 30, 45, 60, 75, 90, 
120, and 180 degrees.


Location Maps with Isocontours
------------------------------

     By popular request, especially from the amateur radio community, I 
have added the Location Map with Isocontours. (Isocontours is a term coined 
by Rob Matson for his SkyMap program and for which he generously supplied 
sample code which I adapted for STSPLUS.) Press the "L" key when the map 
display is present to select this display. The map will be drawn with the 
current magnification/zoom factor and centered on the user's location. The 
usual circle of visibility will be drawn and within that "circle" are seven 
isocontours representing viewing angles of 10 through 70 degrees in ten 
degree increments (five degree increments at maximum magnification 
factors). The projection, orthographic or rectangular, used for the 
Location Map is the projection in use when the "L" key is pressed. The 
balance of the Location Map includes the usual features.
     If you have entered a second location (using F10+F2 from the Main 
Menu), pressing the "L" key when the Location Map is already displayed will 
toggle between your primary location and the second location. The data 
related to your location (Location, Altitude, Azimuth, etc.) is calculated 
with respect to the indicated location. If no second location has been 
entered, pressing the "L" key while the Location Map is displayed will have 
no effect.
     The principal advantage of the Location Map is, of course, the 
isocontours -- lines of equal viewing altitude (line of sight not taking 
into account any refraction near the horizon) from the user's own location. 
The user can immediately tell by inspection whether current or upcoming 
passes will be "good" and what approximate maximum satellite viewing 
altitude can be expected. Amateur radio buffs who need to know if a pass 
will appear above some altitude threshold, say 20 degrees, now have that 
information available visually.
     Since this map mode uses the ZOOM map algorithms, the usual zoom map 
features (PgUp, PgDn, Home, End) are active.


Tracking Station Maps with Isocontours
--------------------------------------

     The Tracking Station Maps with Isocontours are similar to the Location 
Maps except that they use the current TRACKING STATION file locations 
rather than the user's location(s). This feature was implemented at the 
request of folks working on the STS-49 Intelsat Reboost Mission. STSPLUS 
was used operationally by INTELSAT during this mission at their Launch 
Control Center near Washington, DC, and at their five ground tracking 
stations around the world. I subsequently received a letter thanking me for 
the use of the program and saying that it was "critical to mission 
success".
     Pressing the "T" key will select this map mode. STSPLUS calculates 
which of the available tracking stations is nearest to the current 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 37


satellite position and centers that tracking station on the screen. This is 
calculated by determining the angular difference between the sub-satellite 
point and each tracking station. However, this means that depending upon 
the Zoom factor in effect, the satellite may or may not be visible on the 
screen. For example, if the sub-satellite point is in South America and the 
only tracking station in the Western Hemisphere is in the United States, 
the satellite cannot be seen at narrower fields of view.
     The "tracking stations" may be any locations the user chooses and 
includes in the current TRACKING STATION file. Several different tracking 
station files accompany the normal STSPLUS distribution as described in the 
section "NASA Ground Tracking Stations" below. Use Function Key F7 from the 
Main Menu to select the desired file. STSPLUS contains an internal list of 
NASA tracking stations which will be used if the current tracking station 
file cannot be found.
     Maps in this mode are displayed using current map projection. Since 
this map mode uses the ZOOM map algorithms, the usual zoom map features 
(PgUp, PgDn, Home, End) may be used to adjust the field of view (zoom or 
magnification).


Location and Features Labels
----------------------------

     Beginning with Version 9240, STSPLUS can add labels for locations and 
features to all maps. Enable or disable location and features labels using 
Function Keys F10+F3+F9 from the Main Menu. By default, STSPLUS expects the 
geographic location and features data to be in file STSPLUS.LOC. If you 
have created your own .LOC file or the file is not in the current 
directory, use F7 from the Main Menu to specify an alternate file and/or 
path. The supplied file includes 350+ locations (cities) and features 
(oceans and seas), their coordinates, and certain information required by 
the program. The file is standard ASCII "comma-delimited" data. The 
following is a typical data line in the file:

     "London",-.1167,51.5,7,100
      ---+--  ---+-- --+- + -+-
         |       |     |  |  |
         |       |     |  |  +---  Minimum magnification to display
         |       |     |  |
         |       |     |  +------  Color to display label (1 to 15)
         |       |     |
         |       |     +---------  Latitude in degrees
         |       |
         |       +---------------  Longitude in degrees
         |
         +-----------------------  Location or feature name

The label will be displayed if the current magnification is equal to or 
greater than the minimum magnification value specified for that label. All 
label names are converted to upper case for display; avoid the use of 
punctuation other than the period ("."), dash ("-"), or comma (",").
     The minimum magnification factors in file STSPLUS.LOC have been 
carefully selected so that the display is not too "cluttered" at a given 
magnification and so that location or feature names near to each other do 
not usually overlap each other. Some care is required when adding new 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 38


locations to avoid this problem! If you wish to add your own locations 
and/or features, use the supplied STSPLUS.LOC file as a guide and template 
for your changes. Use a standard ASCII editor; word processor users must 
use the "non-document" mode.
     Magnifications are calculated automatically and ranges from 50% to 
4000%, depending upon the map mode in effect. In orthographic map mode the 
magnification factor is displayed as "MAG". In rectangular map modes, the 
displayed ZOOM factor is the approximate field of view and may be converted 
to magnification according to the following table:

    ZOOM    MAG
    -----------
     360     50    World maps
     180    100    Quadrant and Zoom maps
     120    150    )
      90    200    )
      75    240    ) Zoom maps
      60    300    )
      45    400    )
      30    600    )

The "color" is a number from 1 to 15 according to the following table:

     Black   = 0       Gray      = 8
     Blue    = 1       LtBlue    = 9
     Green   = 2       LtGreen   = 10
     Cyan    = 3       LtCyan    = 11
     Red     = 4       LtRed     = 12
     Magenta = 5       LtMagenta = 13
     Brown   = 6       Yellow    = 14
     White   = 7       LtWhite   = 15

The color Black is ignored and is only shown for completeness. If the color 
is a NEGATIVE number, the small circle marking the location of the city or 
feature will NOT be displayed and the label will be displayed centered on 
the coordinates specified. Thus, if the a mountain range, lake, or river is 
to be labeled, you may wish to set the color negative.
     The latitude and longitude are expressed in degrees and decimal 
fractions of a degree; West longitudes and South latitudes must be 
negative. Note that many atlases show a number such as "24.45" which is 
actually 24 degrees and 45 minutes (NOT 24.45 degrees!) and should be 
entered as "24.75" (24 + 45/60). When using multi-line feature labels (see 
file STSPLUS.LOC for examples), labels should be spaced approximately one 
degree apart in latitude for display at a magnification of 100%, less for 
higher magnitudes. All labels are automatically centered with respect to 
longitude.
     There is no restriction on the length of the location name. However, 
avoid long names if possible so as to avoid location names displaying on 
top of one another or "cluttering" the display.

IMPORTANT NOTE: The program performs no error checking on the contents of 
file STSPLUS.LOC. Avoid the use of punctuation other than the period or 
comma. Be sure to use a simple ASCII editor or use your word processor in 
the "Non-Document" mode when editing file STSPLUS.LOC. Very strange results 
can appear if the wrong data are present or the wrong number of items is in 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 39


a data line!


Big Clock Options
-----------------

     In rectangular map projections, STSPLUS defaults to a standard display 
with a text block shown on the lower five lines of the display; three 
different times are shown at the lower left of this display: Launch/Epoch 
date and time, UTC date and time, and local date and time. Pressing 
Function Key F2 while the map is displayed switches between this default 
mode and three Big Clock modes: UTC date and time, local date and time, and 
MET/T+Epoch. Because of display space limitations, big clock options are 
NOT available in orthographic projections.
     For EGA and VGA users, an additional command line option, "/CLK", is 
available which changes the number of lines per screen to 43 and 60 lines 
respectively for rectangular projections. The big clocks are then placed 
below the standard data instead of replacing a portion of the regular data 
area.
     In orthographic modes, VGA monitors ONLY, F2 will display the time at 
the bottom of the data block at the right of the screen. Note that for all 
magnification factors above 100%, the time is shortened to hours and 
minutes because of display space limitations.


Satellite Motion Maps
---------------------

     It is sometimes instructive and interesting to see the ground track 
from the satellite point of view. The Satellite Motion Map, available 
ONLY with EGA and VGA displays, centers the satellite in the display and 
draws the map accordingly. Unlike all other map displays, this mode takes 
advantage of the dual-page capability of the EGA display and the VGA 
display (operating in EGA emulation mode); the current map is always 
displayed and the new map is drawn "off screen" and updated as frequently 
as the capability of the processor will permit. For VGA users, the vertical 
map resolution in this mode is reduced from 400 lines to 280 lines 
(rectangular projections) and from 480 lines to 350 lines (orthographic 
projection).
     Users with slow computers may prefer this display because, once the 
map has been drawn the first time (however long that may take), a complete 
map is always displayed. This is especially true at higher zoom or 
magnification factors where the map is redrawn more frequently.
     The Satellite Motion Map is enabled by pressing the "M" key when the 
map is displayed. The Motion Map will be displayed using the same 
projection as is presently in effect, rectangular (automatically switches 
to zoom) or orthographic. When switching to this map mode, the message 

          Switching to EGA Dual-Page Mode ...

is displayed on the screen while the initial map is being drawn offscreen. 
Thereafter, the map is drawn off-screen and will require the "usual" time 
during which the screen will be unchanged. (My 386DX systems update every 
10 seconds but my 286 systems can only manage every 20 or 30 seconds -- and 
they all have math coprocessors!) The following keys are active when the 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 40


Satellite Motion Map is displayed:

          Home      Zoom=75 (rect) or Mag=100 (ortho)
          End       Return to last zoom/mag
          PgDn      Decrease field of view (zoom in)
          PgUp      Increase field of view (zoom out)
          M         Return to normal map mode (rect or ortho)
          ENTER     Return to Main Menu


Satellite Position and Orbit Projections
----------------------------------------

     The focus of the display, and the reason for program STSPLUS, is to 
show the position of the spacecraft or satellite. For the space shuttle 
(and provided the mission name begins with the letters "STS"), a symbol has 
been chosen which resembles that spacecraft. For all other satellites, a 
symbol has been chosen which resembles the Hubble Space Telescope. In 
either case, the symbol is shown in the following colors (EGA and VGA 
displays only):

          Satellite is sunlit           Bright White
          Satellite is in penumbra      Yellow
          Satellite is in umbra         Dim White

In addition, an asterisk ("*") is shown to the right of "Orbit #" when the 
satellite is sunlit or in penumbra; this will assist users of monochrome 
monitors where colors cannot be distinguished. For better visibility, the 
satellite symbol will normally "blink" on CGA monitors; the symbol may be 
made to blink on any system if desired by pressing the letter "B" while the 
ground track is displayed. Note however that for very slow computers, the 
blink may appear erratic if most of the time is spent performing 
calculations.
     Just seeing the spacecraft or satellite on the map display yields 
information as to its present position. However, for satellite viewing and 
planning purposes, STSPLUS calculates the predicted ground track for 
approximately three hours in the future and the past ground track for 
approximately one and a half hours in the past. The ground track may be 
selected to display as a series of light green dots (future track) or light 
red dots (past track), as a solid light green line, or as a solid light 
green line with yellow dots(future track) and light red dots (past track). 
The dots are plotted at one minute intervals. To select the desired ground 
track display, press Function Key F10 and then press Function Key F5 until 
the desired mode is displayed; the available selections are: OFF, DOTS, 
LINE, and BOTH.
     Note that for satellites in high Earth orbits, the ground track may 
appear as a solid line if the dots are very close together. Unlike prior 
versions of STSPLUS, the ground track is NOT updated (except to re-color 
dots for past track). With automatic map generation off, the map will be 
automatically redrawn every 2.5 hours.



Program STSORBIT PLUS Satellite Orbit Simulation                   Page 41


Satellite Visibility
--------------------

     Satellite visibility, or the ability to see a satellite with the naked 
eye (or binoculars for the truly dedicated), attracts the novice and expert 
alike. It can be a great thrill to point out the Space Shuttle or MIR Space 
Station to a child or a friend as it streaks across the sky where and when 
predicted. Unfortunately, predicting that visibility is more complicated 
than "simple" orbital mechanics and trigonometry; spacecraft altitude, 
position, physical geometry, reflectivity, and attitude with respect to 
both the viewer and the Sun, as well as local atmospheric clarity not to 
mention weather, all contribute to whether or not a satellite may actually 
be seen. Some of these factors are beyond the capabilities of a program 
like STSPLUS. All that can be done is to indicate when conditions are such 
that the satellite MIGHT be sighted visually. STSPLUS estimates viewer 
visibility by calculating that: 

     a)   The satellite is at least partially lighted by the Sun; 

     b)   The Sun is 1.7 degrees or more below the viewer's horizon so that 
          the viewer is in at least partial darkness; and, 

     c)   The satellite is within the viewer's local circle of visibility 
          and is four degrees or more above the horizon.

If all these conditions are met, STSPLUS displays the word "VIS" in the 
data block next to the orbit inclination. To these calculations must be 
added the uncertainties described above. In my experience, the best 
satellite sightings have usually occured when I am between the satellite 
and the Sun, enabling flat surfaces such as solar panels to reflect the 
sunlight back to me.
     Although STSPLUS makes the visibility calculations for any satellite, 
as a general rule only satellites in low Earth orbit, say under 1000 km 
(600 miles) altitude, are likely to be seen with the naked eye. Binoculars 
can extend that range somewhat. Satellites in very high or geosynchronous 
orbits can be seen only with precision optical or radar equipment. Last but 
not least, current 2-line elements must be used for reliable predictions.

                                **********
                                *  NOTE  *
                                **********

          SATELLITE VISIBILITY IS ONLY ACTIVE WHEN THE SOLAR 
          FEATURES ARE ENABLED WITH F10+F3+F8.


User's Circle of Visibility
---------------------------

     Centered around the user's geographic location, and marked with a 
small circle on EGA and VGA systems, is a magenta circle of the approximate 
line of sight visibility for the mission in progress. For rectangular 
projections, the "circle" appears on the display as a circle near the 
Equator and as a distorted circle at higher latitudes. In near-polar 
regions, the circle takes on a very strange shape. The shape is entirely an 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 42


artifact of the map projection; when displayed using the orthographic 
projection, it appear as a true circle near the center of the map. The 
radius of this circle of visibility is calculated for each satellite based 
upon its altitude at the instant the map is first drawn as well as the 
user's elevation above mean sea level and corresponds to "line of sight" 
visibility for that satellite. When a second location has been selected 
using F10+F2, a second circle of visibility will also be drawn for that 
location.
     When audible alarms are enabled (F10+F3+F8 from the Main Menu), tones 
sound 2 minutes before the satellite enters the circle of visibility and 
again 30 seconds before the satellite leaves the circle of visibility. Both 
the primary and secondary locations are monitored, with slightly different 
tones for each. And "up-down" sequence of tones is used prior to entry into 
the circles and a series of tones prior to leaving the circles.
     When a satellite is within the circle, direct visual, radio or radar 
communications with the satellite should be practical. Actual visibility, 
of course, depends upon more than simply whether or not the satellite is 
above the viewer's horizon. Most important is the sun to satellite to 
viewer geometry; the satellite must be in sunlight and the viewer in 
darkness for reasonable visibility. Almost as important is the size and 
geometry of the satellite itself; a large, bright-metal satellite with huge 
solar arrays reflects far more sunlight than a small dark satellite. In 
addition to the satellites themselves, many booster rockets and other 
"spare parts" are orbiting the Earth. Since they are not attitude 
stabilized, booster rockets often are tumbling and may therefore appear 
to flash on and off as they pass over.
     For the Space Shuttle as well as most other satellites with near 
circular orbits, the circle of visibility calculations are reasonably 
accurate; however, the position of the sun and the effect of atmospheric 
refraction are not taken into account, only whether or not the satellite is 
in line of sight view from the observing location. For highly eliptical 
orbits, however, the accuracy is substantially degraded since the radius of 
the circle of visibility changes dramatically depending upon whether the 
satellite is nearer apogee or perigee at the time the calculation is made, 
and the period of the orbit. In the course of a single orbit, the altitude 
of such a satellite may change by thousands of miles. Satellite "DE 1", 
usually included in the TLEnnn.TXT 2-line elements file, is in a highly 
elliptical orbit with long period and illustrates the problem.


Spacecraft Circle of Visibility
-------------------------------

     The spacecraft circle of visibility is calculated dynamically using 
the same alrorithm as for the user's circle of visibility. Like the user's 
circle, the spacecraft circle may appear on rectangular projections as an 
odd shape because of the scaling factors used by the map projection. The 
difference is that the spacecraft circle moves with the spacecraft and 
illustrates the approximate area visible from the spacecraft at any given 
moment. The circle is updated every ten seconds (or as frequently as the 
processor will permit). Comparisons using a VGA display system during the 
STS-35/ASTRO-1 mission in December, 1990 confirmed that the circle shown is 
quite close to that shown by one of the special graphics displays 
occasionally seen on NASA Select Television as well as the actual horizon 
view seen from the payload bay television cameras.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 43




SUN and Solar Features
----------------------

     Many types of observations, especially Earth observations, often 
require that the target or terrain be in sunlight. The performance of solar 
panels and certain other instruments on a spacecraft is dependent upon 
whether or not the Sun is in view. Also, it is usually impossible to 
visually see a spacecraft which is not in sunlight. The solar terminator is 
a series of yellow points on the display which represent the line at which 
the center of the Sun is at an observer's horizon for Mean Sea Level. 
Although a quick glance at the clock should suffice to determine which side 
of the terminator line is in sunlight and which in darkness, EGA and VGA 
systems also display the Sun as a small yellow circle. 
     The terminator as displayed by STSPLUS is sometimes confused with a 
line denoting sunrise and sunset. Two factors make the terminator only an 
approximation: first, the terminator is based upon the center of the Sun, 
while actual sunrise and sunset are calculated using the upper limb of the 
Sun; and second, the terminator is calculated for Mean Sea Level rather 
than a specific local elevation. These two factors combined can result in a 
difference of up to ten minutes when the times are compared against 
published values or those calculated by my program ASTROCLK, sunrise being 
earlier and sunset being later.
     The Sun and solar features are enabled and disabled using F10+F3+F8 
from the Main Menu. Since these features -- especially the terminator -- 
require some calculation and drawing time, users with slower computers may 
wish to disable these features for faster screen updates. The following 
features are included:

Sun:           A yellow circle is plotted at the sub-solar point, the 
               geographic coordinates directly beneath the current position 
               of the Sun. The position of the Sun is recalculated every 10 
               seconds and the display is updated every 60 seconds. (Not 
               shown on CGA and HGC displays.)

Terminator:    A dotted yellow line is plotted for the solar terminator, 
               that point on the Earth at which the center of the Sun is at 
               the horizon. The terminator is partially updated every 10 
               seconds and is fully updated every 60 seconds.The terminator 
               is shown for Mean Sea Level and does NOT take into account 
               the non-spherical shape of the Earth.

Lighting:      The current spacecraft lighting is shown using color for the 
               satellite icon, and in the data block (to the right of 
               "Orbit #:") and displayed using the following symbols and 
               colors:

               *    Bright White   Full sunlight
               +    Yellow         Partial sunlight (penumbra)
               -    Light Red      Refracted sunlight
                    White          Full shadow (umbra), no symbol

               Note that Yellow and Light Red will display as Bright White 
               or shades of gray on monochrome monitors.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 44



               Solar lighting conditions are updated every second or as 
               rapidly as the speed of the processor will permit. In order 
               to minimize calculation delays during ground track plotting, 
               the event times for orbital sunrise and sunset are 
               approximated. The dynamic lighting calculations, used to 
               plot the color of the spacecraft icon, are more precise. 
               Typical errors due to the simplified algorithm, are on the 
               order of 10 seconds.

SUN Timer:     When Event Timers are enabled, the orbital sunrise (AOS) and 
               sunset (LOS) times are shown. A blank AOS or LOS timer 
               indicates the event will not occur within the next four 
               hours. An asterisk ("*") to the left of "SUN" indicates 
               sunlight is on the satellite:

                       AOS    LOS
               *SUN  73:20  37:40

               In this example, the satellite is in sunlight. Orbital 
               sunset will occur in 37:40 and the next orbital sunrise will 
               occur in 73:20.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 45


TDRS and Real Time Satellite Features
-------------------------------------

     TDRS and Real Time Satellite features are available only on EGA and 
VGA monitors. These features permit up to thirty two additional satellites 
to be tracked in near real time. Satellites to be tracked are designated by 
the user as "static" (geosynchronous or geostationary) and "real time" 
(satellites whose sub-satellite point changes substantially with time). 
Static satellites are only plotted when the map is redrawn; real time 
satellites are plotted every 10 seconds (X1 and X10), or every 60 seconds 
(X60), or as often as the processor can complete the required calculations.
     When TDRS and Real Time Satellite coverage is enabled (F10+F3+F2), all 
active TDRS satellites (Tracking and Data Relay Satellites), used for most 
communications to and from the Space Shuttle, the Hubble Space Telescope, 
and other active spacecraft, are shown as a dot inside a small circle near 
the Equator (provided they have been included in the current TDRS and Real 
Time Satellite configuration). Use F6 from the Main Menu to display and/or 
modify that configuration. See the text section on Function Key F6 for a 
complete description of Static and Real Time satellites.
     As of August, 1993, there are five TDRS satellites in geosynchronous 
orbit. The primary satellites consist of TDRS East ("TDRS 3") at 
approximately 41 degrees West longitude and the TDRS West Cluster 
consisting of two satellites, TDRS West ("TDRS 4") and TDRS Spare ("TDRS 
1") at approximately 174 and 170 degrees West longitude respectively. The 
TDRS Spare satellite has partially failed but is used occasionally as a 
backup; this satellite is also low on propellant and is allowed to drift 
considerably with an inclination of about 7 degrees. "TDRS 2" has also 
partially failed and is currently parked at approximately 62 degrees West 
longitude and is presently dedicated to downlinking data from GRO, the 
Gamma Ray Observatory, whose tape recorders have failed. "TDRS 5" is the 
most recent satellite launched, is fully operational, and is parked at 
about 138 degrees West longitude as an on-orbit spare. Users should check 
the current positions of the TDRS satellites since they are periodically 
moved or reassigned.
     Each TDRS location provides communications coverage for almost half 
of the Earth for low Earth orbits and essentially full time coverage for 
higher orbits. However, since the NASA Ground Terminals are located at 
White Sands, New Mexico, the coverage has been slightly overlaped to 
provide good ground communications at White Sands. This, in turn, means 
that there is a narrow band, known by NASA as the Zone of Exclusion (marked 
"ZOE" on the screen), off the East coast of Africa which is not covered by 
either primary TDRS for low Earth orbits. Two red "circles" on the display 
show the limits of coverage for each primary TDRS satellite. Each circle, 
whose shape may be quite distorted when using rectangular projection, 
encloses an area where the TDRS satellite is out of range of the primary 
satellite being tracked and is centered on the opposite side of the Earth 
from the TDRS satellite's position.
     While the ground track is being calculated, STSPLUS also calculates 
the times for acquisition of signal (AOS) and loss of signal (LOS). When 
TDRS coverage is enabled, these times are displayed for TDRS East and TDRS 
West. The method used for the calculation of the TDRS coverage is usually 
accurate to about 10 seconds (assuming accurate 2-line elements for the 
satellite and for the TDRS). However, spacecraft attitude can cause loss of 
TDRS communications at unexpected times. When Event Timers are enabled, 
STSPLUS calculates AOS and LOS for four hours (240 minutes) from the time 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 46


the map is drawn. If a time is beyond that limit (or if the condition does 
not occur), the time is left blank.
     Each time is presented in the form of a countdown clock, minutes and 
seconds, until the next occurence of the condition:

         *TDRE AOS/LOS  72:42  50:42     (for rectangular projections)
         *TDRW AOS/LOS  45:42  22:42

                          AOS    LOS
                *TDRE:  72:42  50:42     (for orthographic projections)
                *TDRW:  45:42  22:42

An asterisk ("*") is shown to the left of the satellite name if AOS is in 
effect. For rectangular projections, these data are displayed in the lower 
right portion of the map. For EGA and VGA users, however, the data may be 
displayed in the lower section of the data block by pressing F2 while the 
map is displayed until MET/T+E is displayed. For orthographic projections, 
the data are part of the standard data block at the right of the screen.
     The clocks for each TDRS are color coded to indicate the current 
status: GREEN when the satellite is in communication, and RED when the 
satellite is out of range of the TDRS. Two minutes prior to a change in 
status, the appropriate clock color changes to YELLOW. Users with 
monochrome monitors must observe the presence or absence of the asterisk to 
determine the status.
     STSPLUS can sound an audible alarm (three beeps) 30 seconds prior to 
TDRS AOS or LOS. Use F10+F3+F8 to enable or disable the audible alarms.
     Most satellites which utilize the TDRS system for communications are 
in low Earth orbits (generally below 1500 km). However, other satellites 
may also use the TDRS system for regular or backup communications. The 
NAVSTAR Global Positioning Satellites (GPS), with orbital altitudes of 
about 11,000 nautical miles (20,000 kilometers), are an example. For such 
high orbits, the coverage by each TDRS satellite is nearly continuous.
     As noted above, there are currently five TDRS satellites in orbit as 
of mid 1993, TDRS 1 through TDRS 5. (These numbers are those currently used 
by US Space Command in their 2-line elements. NASA sometimes uses different 
numbers corresponding to the original launch letters as shown in the 
following chart. TDRS "B", which should have become "TDRS 2", was lost in 
the Challenger accident.) As of July, 1993, the TDRS assignments are:

      TDRS#  *   NORAD#     Long    Description
     -----------------------------------------------------------------
     TDRS 1 (A)   13969    -170W    TDRS West Spare, used occasionally
     TDRS 2 (C)   19548     -62W    Dedicated to Gamma Ray Observatory
     TDRS 3 (D)   19883     -41W    TDRS East (STSPLUS default)
     TDRS 4 (E)   21639    -174W    TDRS West (STSPLUS default)
     TDRS 5 (F)   22314    -138W    On-orbit spare

     * Original NASA letter designation at launch

STSPLUS will use TDRS 3 and TDRS 4 by default and approximate positions as 
of July, 1993 are automatically saved in file STSPLUS.INI. Note that some 
2-line element files (including TLEnnn.TXT) often refer to the TDRS 
satellites using numbers 1 through 5 or letters A through D or E. Use the 
NORAD numbers to be certain that you display the correct satellite.
     TDRS satellites do change position and/or assignment periodically for 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 47


one reason or another. Users who wish the most accurate TDRS positions and 
AOS/LOS data should periodically update the default positions by using the 
automatic update feature with F2 from the Main Menu to read and update the 
2-line elements.


Ground Tracking Stations and .TRK files
---------------------------------------

     NASA maintains a number of ground tracking stations around the world. 
Some of these tracking stations are essential for the ascent or landing 
phases of a space shuttle flight; others are used for in-flight 
communications. File STSPLUS.TRK contains the information for these ground 
tracking stations. Other files with filetype .TRK contain the information 
for other launch and/or tracking stations.
     Each ground tracking station is shown as a small symbol surrounded by 
a brown or light yellow "circle of visibility" which gives the approximate 
area of antenna coverage and shows how small a proportion of each orbit can 
be monitored without the TDRS system. When for some reason the TDRS system 
is down (as has occurred during infrequent computer failures at White 
Sands, New Mexico, the TDRS Ground Station), these ground tracking stations 
become the only means of communication with the Space Shuttle. (Another 
unexpected method was demonstrated during a 1992 space shuttle mission when 
the SAREX, Shuttle Amateur Radio EXperiment, was used during a complete 
loss of normal communications!) Because of budget constraints, many of 
these ground tracking stations may be (or have already been) shut down. 
Some, such as MIL and BDA (see list below) will be retained because they 
are required for the ascent phase of a space shuttle mission. Others, such 
as HAW, CTS and GWM, are operated jointly with, or independently by, the 
U.S. Air Force. NASA is not always consistent as to the abbreviations used 
for these tracking stations; on NASA Select TV, Gwan, Hawaii, and 
Vandenbert are usually shown as GTS, HTS, and VTS respectively.
     When using rectangular map projections, the shape of the antenna range 
"circle of visibility" varies as a function of the latitude and is an 
artifact of the map projection; when projected on a sphere, as is the case 
with orthographic projection, they are true circles. In order to avoid 
cluttering the display with countless meaningless lines, tracking station 
circles of visibility are shown only if that circle has an angular diameter 
of 90 degrees or less. 
     The following table lists the internal ground tracking stations as of 
early 1989 which are shown along with their abbreviations and approximate 
map coordinates (longitude, latitude):

          MIL     -81,28         Merritt Island, FL
          BDA     -64,32         Bermuda
          DKR     -17,14         Dakar, Senegal
          ACN     -14,-8         Ascension Island
          MAD     -5,41          Madrid, Spain
          IOS      56,-5         Indian Ocean
          HAW     -156,20        Hawaii
          GWM      143.33,14     Guam
          VAN     -120.57,34.73  Vandenberg, CA
          YAR      115,-29       Yarragadee, Australia
          CAN      149,-36       Canberra, Australia
          GDS     -116.88,35.93  Goldstone, CA

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 48


          CTS     -105,38        Colorado Springs, CO
          AGO     -71,-34        Santiago, Chile
          NGT     -106,33        White Sands, NM

     STSPLUS first checks for the presence of file STSPLUS.TRK for its 
ground tracking station information. This is the default TRACKING STATION 
filename used if no other selection has been made using F7 from the Main 
Menu. If that file is present, its data is used instead of the internal 
data above. The supplied STSPLUS.TRK has the following format:

          "Maui, Hawaii",-156.7,20.9,0,"HAW"
          "Vandenberg, CA",-120.5667,34.7333,112,"VAN"
          "White Sands, NM",-106,33,0,"NGT"
          "Colorado Springs, CO",-105,38,0,"CTS"
          "Merritt Island, FL",-81,28,0,"MIL"
          "Santiago, Chile",-71,-34,0,"AGO"
          "Bermuda",-64,32,0,"BDA"
          "Dakar, Senegal",-17,14,0,"DKR"
          "Ascension Island",-14,-8,0,"ACN"
          "Madrid, Spain",-5,41,0,"MAD"
          "Indian Ocean Stn",56,-5,0,"IOS"
          "Yarragadee, Australia",115,-29,0,"YAR"
          "Guam",143.3333,14,0,"GWM"
          "Canberra, Australia",149,-36,0,"CAN"

     These files are ASCII and may be prepared or edited with any standard 
ASCII editor; if using a word processor, select the "non-document" mode. 
Five items are required for each location; the longitude and latatude are 
expressed in degrees and fraction of a degree, elevations above Mean Sea 
Level are expressed in meters, and names or abbreviations are included in 
double quotation marks. The following example illustrates the .TRK file 
format:

          "Merritt Island, FL",-81.0,28.0,0,"MIL"
          --------+----------- --+-- --+- + --+--
                  |              |     |  |   |
                  |              |     |  |   +--- 3-Letter Abbreviation
                  |              |     |  +------- Elevation (meters)
                  |              |     +---------- Latitude (degrees)
                  |              +---------------- Longitude (degrees)
                  +------------------------------- Location Name

     For those interested in the Russian space program, a list of Russian
ground tracking stations is provided in file CIS.TRK (data courtesy 
Ellwood Marshall). With the breakup of the Soviet Union, some of these 
installations may no longer be active or the name may have changed.

          "Tyuratam Cosmodrome",63.3392,45.9235,0,"TYR"
          "Kaliningrad Cntrl Ctr",37.816,55.916,0,"KAL"
          "Plesetsk Cosmodrome",40.7,62.75,0,"PLS"
          "Petropavlovsk Russia",158.933,53.216,0,"PTR"
          "Tbilisi Georgia",44.75,41.66,0,"TBL"
          "Ulan Ude Russia",107.683,51.983,0,"ULN"
          "Ussuriysk Russia",132.15,43.8,0,"USS"
          "Yevpatoria Ukraine",33.3666,45.2166,0,"YEV"

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 49



     Other nations also have facilities for satellite launches. As of early 
1993, file SPACENTR.TRK includes the following locations:

          "Alcantara LC Brazil",-44.3999,-2.3999,0,"ALC"
          "Esrange,Kiruna Sweden",21.067,67.883,0,"ESR"
          "Jiuquan Space LC China",100.033,40.83,0,"JIU"
          "Kagoshima Center Japan",131.083,31.25,0,"KAG"
          "Kourou Space Ctr Fr.Gu",-52.7669,5.23,0,"KOU"
          "San Marco Platform",40.2,-2.9329,0,"SMP"
          "Sriharikota Ctr India",80.25,13.78,0,"SRI"
          "Tanegashima SC Japan",130.967,30.4,0,"TAN"
          "Xichang Space LC China",102.217,27.967,0,"XUC"

     The first mission of Endeavour, STS-49, was in May, 1992. This 
dramatic and exciting mission captured the INTELSAT VI (F3) satellite, 
stranded in a useless orbit by its booster rocket failure since January, 
1990, and attached a new booster rocket which placed the satellite in its 
proper orbit. STSPLUS was used operationally during the mission by 
Intelsat, another "first" for the program. Intelsat used its own ground 
tracking stations for communications with INTELSAT VI (F3); the ground 
stations which participated in the mission are listed in file INTELSAT.TRK 
(information courtesy Dee Smith):

          "Paumalu, Hawaii",-158.0342,21.6711,157.86,"PAU"
          "Tangua, Brazil",-42.7845,-22.7442,35.38,"TAN"
          "Jatiluhur, Indonesia",107,-6.5213,161.49,"JAT"
          "Perth, Australia",115.25,-31.8,0,"PER"
          "Gandoul, Senegal",-17.4745,14.43,0,"GAN"

     These TRK files are standard ASCII files and may be edited with any 
editor; word processor users be sure to use the ASCII or non-document mode. 
The files use a standard comma-delimited format as shown; positions are 
given in longitude (degrees) and latitude (degrees), rounded to the nearest 
degree. A maximum of 25 ground stations is permitted. The use of TRK files 
is not restricted to tracking stations, of course. So long as the correct 
data format is observed, any desired location may be included in the 
tracking station file up to the maximum of 25 locations.


Event Timers and Audible Alarms
-------------------------------

     STSPLUS is often operated for long periods of time with minimum 
operator attention or intervention. Users may perform other tasks while the 
satellite display is active and while awaiting some subsequent event of 
interest. Event timers are displayed for the selected events if they will 
occur within approximately four hours of the time that the map is drawn; if 
an event will not occur within that time, the event is blank. Audible 
alarms serve to alert the user to upcoming selected events. The event 
timers are enabled with F10+F7 from the Main Menu. Audible alarms are 
enabled with F10+F8 from the Main Menu and require also that the event 
timers be enabled. All events are termed "AOS" (Acquisition of Signal or 
Source) or "LOS" (Loss of Signal or Source) and are generally calculated 
for line of sight conditions.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 50


     Each phenomena which may be timed has an associated AOS and LOS timer 
which displays the hours and minutes ("HHH:MM") remaining until the next 
event if that event will occur within the next four hours (240 minutes), 
one hour past the last time for which the ground track is plotted. The 
current status of the signal or source is indicated by the color of the 
timer digits and the presence or absence of an asterisk ("*") to the left 
of the event name: GREEN indicates signal or source acquisition, and RED 
indicates signal or source loss. Two minutes prior to an event, the timer 
for that event will change from the signal status color (GREEN or RED) to 
YELLOW to visually alert the user. Users with monochrome monitors will be 
unable to distinguish these color changes, of course, but can determine the 
current signal status using the asterisk indicator.
     All calculations for upcoming events are made each time the ground 
track is drawn on the display and will affect the time required to prepare 
the display, especially on slower computers. In order to minimize these 
calculation delays, the event calculations for orbital sunrise and sunset 
use a simplified algorithm which does not take into account the non-
spherical shape of the earth (unlike the dynamically calculated spacecraft 
lighting features which are more accurate). Orbital sunrise and sunset are 
the times that the spacecraft transitions between refracted sunlight 
(sunlight refracted through the Earth's atmosphere) to partial sunlight 
(illumination from only a portion of the solar disk); this corresponds to 
the transitions between RED and YELLOW color on the satellite icon and 
illumination symbols respectively. The errors resulting from the simplified 
algorithm are usually less than plus or minus 10 seconds; because of the 
more oblique angles and geometry involved, higher errors are usually 
associated with higher inclination orbits.
     When no secondary location is selected, the headings "AOS" and "LOS" 
will appear in orthographic modes; the headings do not appear in 
rectangular modes or in orthographic modes when a secondary location is 
selected in order to make room for the additional line of data. Typical 
Event Timers are shown in the following examples.

For orthographic projections:

          *STN   95:15   6:21           AOS now in effect
                                        AOS will next occur in 95:15
                                        LOS will occur in 6:21

           STN   23:47  45:18           LOS now in effect
                                        AOS will occur in 23:47
                                        LOS will next occur in 45:18

and similarly for rectangular projections:

          *TDRW AOS/LOS  85:14  33:43   AOS now in effect
                                        AOS will next occur in 85:14
                                        LOS will occur in 33:43

           TDRW AOS/LOS  14:21  57:32   LOS now in effect
                                        AOS will occur in 14:21
                                        LOS will next occur in 57:32

except the primary location AOS/LOS, which is unlabeled in rectangular 
projections and appears at the upper right of the data block (immediately 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 51


to the right of MET/T+E):

          * 89:39   1:27                AOS now in effect
                                        AOS will next occur in 89:39
                                        LOS will occur in 1:27

            70:15  76:38                LOS now in effect
                                        AOS will occur in 70:15
                                        LOS will next occur in 76:38

     The following events may be timed and will cause an audible alarm if 
audible alarms are enabled and the appropriate events are enabled:

     Local Visibility    For the primary location ("STN" or "STN1"): three 
                         sets of up/down tones two minutes prior to AOS and 
                         five tones thirty seconds prior to LOS. For the 
                         secondary location ("STN2" if enabled): two sets 
                         of up/down tones two minutes prior to AOS and four 
                         tones thirty seconds prior to LOS. Refers to the 
                         times the satellite enters or leaves the local 
                         circle of visibility.

     TDRS Acquisition    ("TDRE" or "TDRW" if enabled) Three short tones 
                         thirty seconds prior to AOS or LOS. Refers to the 
                         times the satellite acquires or loses the ability 
                         to communicate with either of the programmed 
                         Tracking and Data Relay Satellites.

     Orbital Sunrise/set ("SUN" if enabled) Two tones thirty seconds prior 
                         to approximate orbital sunrise or sunset. Refers 
                         to actual line of sight solar contact; refracted 
                         sunlight is not included. 

The characteristics of the audible tones have been selected to allow the 
user to uniquely identify the AOS or LOS event that is about to happen.
     STSPLUS is now "aware" of program RighTime by Tom Becker and its use 
is recommended for accurate timekeeping. Audible alarms in prior versions 
would perform unpredictably when RighTime was active because they use the 
hardware clock's timer functions (which RighTime also uses). STSPLUS now 
detects RighTime and temporarily disables RighTime while an audible alarm 
is being generated and then re-enables RighTime after the alarm has 
completed, restoring precise timekeeping. With RighTime active, alarms are 
generated in foreground, which may cause a slight delay in screen updating.


                               *************
                               *  CAUTION  *
                               *************

     STSPLUS expects RighTime Version 2.5+; performance with prior 
     versions of RighTime may yield unpredictable results. If using a 
     prior version of RighTime, do NOT enable audible alarms!


     If RighTime is not present or is not detected, the audible alarms are 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 52


generated in background as in prior versions. This usually causes the loss 
of several clock ticks in the DOS software clock for each audible alarm. 
Although the time loss per audible alarm is very small, the cumulative 
error may become significant over extended time periods.


Pausing the Ground Track Display
--------------------------------

     Pressing F6 will cause the ground track display to "freeze" at the 
current time. This is called PAUSE mode. This permits closer examination of 
the data and/or display at any given time and to "move" the display forward 
and backward in time. Note that the pause takes effect AFTER the next 
second tick on the system clock; thus, if you wish to pause at 01:00 (one 
minute exactly on one of the clocks), press F5 when the display reads 
00:59.
     After pressing F6, the following message will appear near the lower 
right of the screen:

          PAUSE...Press ENTER

This reminds the user that PAUSE is in effect and to press ENTER to 
resume normal operation. When normal operation is resumed, the time 
continues from its present value, as if you had set SIMULATED TIME using 
F8+F3 or F8+F4 from the Main Menu. To return to REAL TIME, use F8+F1 from 
the Main Menu.
     While PAUSE is in effect, the "+" and "-" keys may be used to advance 
or retard the current time by the amount of the current time step. You may 
also use the "=" key instead of the "+" key to avoid pressing the SHIFT 
key. The only other key active in PAUSE mode is F4, which may be used 
to adjust the "time step" by pressing the key until the desired time 
multiplier is displayed at the upper right of the screen. Time multipliers 
of "X1" (no message displayed), "X10", and "X60" are selected in 
succession. The default time step is 1 second.
     Note that the automatic map generation feature is also used in PAUSE 
mode; automatic map generation may be enabled or disabled in the 
rectangular projections (use the TAB key) and is ALWAYS enabled in 
orthographic projections. Thus, when the satellite is moved near the edge 
of the display, the map may be redrawn if the appropriate point is reached.
     If you wish to synchronize the time used by STSPLUS to some other 
source (such as the slightly delayed orthographic displays presented from 
time to time on NASA Select TV), you may also use PAUSE mode for this 
purpose. Simply pause the display, use the "+" or "-" keys to adjust the 
time slightly ahead of the time to which you wish to synchronize. Then 
press ENTER when the times agree. Time can only be synchronized in this 
manner to plus or minus one second. If you need higher precision, set 
SIMULATED TIME using F8+F3 or F8+F4 from the Main Menu.


Switching between MET and T+Epoch
---------------------------------

     STSPLUS by default displays the time elapsed since the epoch date of 
the elements in the upper right portion of the data block unless the launch 
date and time are included in file STSPLUS.LTD, in which case Mission 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 53


Elapsed Time (MET) is the default. This marked on the display as "T+Epoch" 
or "T+E" and "MET" respectively. While T+Epoch is not of particular value 
for satellite viewing purposes, it does indicate the relative age of the 
orbital data. As a general rule, especially for lower Earth orbits, the 
effects of orbit decay make position predictions less accurate as time 
passes. Data which are more than 10 or 20 days old may produce less 
accurate positions.
     For a space shuttle mission, however, all mission events are scheduled 
against the mission timeline and are reckoned in Mission Elapsed Time 
(MET), the time elapsed since launch. It is therefore useful to be able to 
display MET during the course of a mission or to review the flight post-
mission. Unfortunately, the standard NASA/NORAD 2-line element format does 
not include the launch time and launch date and therefore this information 
must be secured independently and manually entered into STSPLUS. Once 
entered, STSPLUS saves the information in file STPLUS.LTD.
     Once the ground track map is displayed, the F5 command may be used to 
switch the display between Time Since Epoch ("T+Epoch" or "T+E") and 
Mission Elapsed Time ("MET").
     The F5 command checks that you have already entered the launch time 
and launch date or that it has been read from file STSPLUS.LTD. If no 
launch time and date are present, the command will have no effect. Press 
ENTER to return to the Main Menu and press F5 to enter launch time and 
launch date.


Using FAST Time
---------------

     Press F4 while the map is displayed to use FAST time. FAST TIME is a 
variation of SIMULATED TIME which automatically advances the time displayed 
by 10 or 60 seconds, as indicated at the upper left of the screen. Press F4 
again to change the time step; when "(X10)" or "(X60)" is NOT displayed, 
the time step is one second. The actual time increment is a function of the 
computer's speed. For fast computers, the time increment will usually be 10 
or 60 seconds but may vary by a second occasionally; for slower computers, 
the time increment may be somewhat longer. FAST time is disabled when PAUSE 
mode is in effect and for the Satellite Motion Map.
     FAST time may be used to advance the display to a future time and for 
demonstration purposes. Once the desired time has been reached, simply 
press F4 until no time step is displayed at the upper left of the screen 
and time will advance normally. Note that FAST time sets the program to 
SIMULATED TIME; to restore "real time", press F8+F1 from the Main Menu. The 
Main Menu also indicates when SIMULATED TIME is in effect: the words 
"Current Time" will appear at the left of the times at the top of the 
screen when real time (the time your DOS clock is using) is in effect; the 
words "Simulated Time" appear when a simulated time is in effect.



On-line Help
------------

     An on-line Help Screen is available during the ground track display 
to remind the user of the available functions and which keys to press to 
trigger those functions. When the ground track display is active, press 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 54


Function Key F1 to display the Help Screen in the lower portion of the 
display. The following help screen will appear in rectangular modes:

 F1=Resume Data   F6=Pause (+,-)    TAB=Auto Maps On/Off  L=Location Maps
 F2=Select Clocks F7=Circle of Vis    W=World Maps        T=Tracking Maps
 F3=Printer Log   F8=SUN and Term     Q=Quadrant Maps     M=Motion Map
 F4=Time Step     F9=Units (nm/km)    Z=Zoom Maps:        O=Orthographic
 F5=MET/T+Epoch  F10=Sat Coordinates    Home,PgUp,PgDn    STSPLUS Ver 9338

The help screen in orthographic modes is similar but in a vertical format 
at the right side of the screen.
     The ground track display will continue to be updated in real time 
while the help screen is displayed. If only the graphical display of the 
ground track is of interest, the help screen may be kept on the display 
continuously. Press Function Key F1 again to return to the normal data 
display in the lower portion of the screen. Note that the Help Screen is 
disabled when the Motion Map is displayed.



Program STSORBIT PLUS Satellite Orbit Simulation                   Page 55


ACTIVE KEYS DURING GROUND TRACK DISPLAY
---------------------------------------

     The following table lists the various keys which are active when the 
ground track display is shown on the screen. Some of these features are 
more fully described elsewhere.

   ENTER  Return to Main Menu (cancel the simulation).

      F1  On-line HELP. Press F1 to display a help screen in the lower 
          portion of the screen. Press F1 again to resume normal data 
          display.

      F2  Selects the Big Clock mode. These modes are selected in the 
          following order:

               0    No clock displayed
               1    UTC date and time
               2    Local date and time
               3    STN/TDRS AOS/LOS and MET or T+Epoch (select with F5)

          Note that not all computers (especially older CGA systems) will 
          display the extended graphics characters used for the large clock 
          characters. The symptom of this problem is that the lower left 
          portion of the data block is mostly blank after pressing F2. If 
          you have this problem and your computer is running DOS 3.x or DOS 
          5.0, enter the command "GRAFTABL" at the DOS prompt before 
          running STSPLUS or include the line "GRAFTABL" in your 
          AUTOEXEC.BAT file; this sets the "code page" to enable the 
          computer to display the extended graphics characters. [The 
          program GRAFTABL.COM is included as part of DOS in most cases.]

      F3  Enable or disable printer logging. If logging is enabled, the 
          word LOG appears in the lower right of the screen. Be sure the 
          printer is turned on BEFORE using the L command. The "L" command 
          automatically enables the display of ascending and descending 
          node information.

      F4  Toggle FAST mode from x1 to x10 to x60 to x1, etc. When either of 
          the fast modes is enabled, "(x10)" or "(x60)" will appear at the 
          upper right of the data block in red. This feature operates in 
          both the normal (real or simulated time) and PAUSE modes. When 
          x10 or x60 fast modes are used, automatic map generation is 
          disabled in rectangular projections; use the TAB key to restore 
          automatic map generation.

      F5  Switches the elapsed time between "T+Epoch" and "MET". If no 
          launch time and date have been entered, this command will have no 
          effect.

      F6  Enable PAUSE mode. The plot is frozen at the current position and 
          the "+" and "-" keys are enabled. (The "=" key may be used 
          instead of the "+" key to avoid use of the SHIFT KEY.) Press 
          ENTER to resume normal operation using the current simulated 
          time.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 56



      F7  Enable or disable the spacecraft circle of visibility.

      F8  Enable or disable the SUN, solar terminator, and spacecraft 
          lighting feature. NOTE: The SUN and spacecraft lighting are not 
          available on CGA systems.

      F9  Change units of distance between kilometers (km) and nautical 
          miles (nm).

     F10  Change satellite coordinates between Altitude and Azimuth, Right 
          Ascension and Declination, and Geocentric Rectangular (XYZ) 
          systems.

       +  During PAUSE mode only, moves the satellite to the NEXT 
          calculated position based upon the FAST mode then in effect: 
          simulated time is advanced 1, 10, or 60 seconds. (NOTE: The "=" 
          key may be used instead of "+" to avoid the SHIFT KEY.)

       -  During PAUSE mode only, moves the satellite to the PREVIOUS 
          calculated position based upon the FAST mode then in effect: 
          simulated time is backed up 1, 10, or 60 seconds.

     TAB  Enable or disable automatic map generation. Automatic map 
          generation is ALWAYS enabled in orthographic modes. When 
          automatic map generation is enabled in rectangular map modes, the 
          letter "A" will appear in the upper right of the display screen. 
          Pressing the TAB key will always cause the map to be redrawn.

    PgUp  When in one of the zoom modes, increases the field of view up to 
          a maximum of 180 degrees. Press rapidly to execute multiple zoom 
          steps without redrawing the map for each keypress.

    PgDn  When in one of the zoom modes, decreases the field of view down 
          to a minimum of 30 degrees. Press rapidly to execute multiple 
          zoom steps without redrawing the map for each keypress.

    Home  When in one of the zoom modes, returns the field of view to 75 
          degrees (rectangular projections) or the full globe (orthographic 
          projections).

     End  When in one of the zoom modes, returns the field of view to the 
          last zoom factor used prior to pressing the HOME key.

       B  Toggle the BLINK mode of the satellite symbol between blinking 
          and steady. NOTE: On most systems, the satellite symbol will 
          appear to blink very briefly as it is erased and redrawn even 
          when BLINK is OFF.

       O  Select Orthographic Projection (the LETTER "O" not the digit 
          zero). PgUp, PgDn, Home, and End are active to select the 
          magnification.

     W,0  Select World Map display, showing the full world from +85 degrees 
          North latitude to -85 degrees South latitude using rectangular 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 57


          projection. If automatic map generation is disabled, pressing "W" 
          or "0" will toggle between the two world map displays.

       Q  Select Quadrant Map display, showing 180 degrees field of view 
          (rectangular projection) and selected so as to approximately 
          center the satellite.

      1-9 Select the indicated Quadrant Map. Automatic map generation is 
      !@# disabled when a specific quadrant map is selected. See the chart
          in the section Quadrant Maps for the map numbers.

       Z  Select Zoom Map display, showing from 180 to 30 degrees field of 
          view (rectangular projection) and selected so as to approximately 
          center the satellite. The default is 75 degrees.

       L  Select Location Map display, showing concentric isocontours for 
          your location. If a second location has been enabled, press "L" 
          again for that location.

       T  Tracking Station Map display, showing concentric isocontours for 
          the tracking station closest to the current ground track position 
          of the satellite using the current projection. Uses the data in 
          the current TRACKING STATION file to select the tracking 
          station(s); if the file is not found, STSPLUS defaults to an 
          internal set of tracking stations. Use F7 from the Main Menu to 
          select the TRACKING STATION filename.

       M  Satellite Motion Map display, available on EGA and VGA systems 
          only. Displays a map with the satellite centered using the map 
          projection in effect when the key is pressed. In rectangular 
          modes, the map is shown in zoom. Maps are drawn "off screen" and 
          a complete map is always displayed. The map is updated every 10 
          seconds or as rapidly as the computer processor will permit. 
          While the Satellite Motion Map is displayed, the following keys 
          are active: ENTER, "M", "Home", "End", "PgUp", and "PgDn"; these 
          keys perform the same functions as during the normal display 
          except that the "M" key cancels the Satellite Motion Map and 
          returns to normal display.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 58


STSORBIT PLUS MAIN MENU
-----------------------

     Once the map coordinates have been stored internally, STSORBIT PLUS
presents its Main Menu:



                              Program STSORBIT PLUS

                  Space Shuttle and Satellite Orbit Simulation
                                  Version 9338

                   Current time:  15:47:28 PST   23:47:28 UTC
                   Current date:    03/11/1993     03/11/1993

         F1     Convert Keplerian Data to 2-Line Format
         F2     Read NASA/NORAD 2-Line Elements       (.TXT/.TLE Files)
         F3     Pass Predictions and Data Output
         F4     Tabular Satellite Positions      (TRAKSTAR by TS Kelso)
         F5     Set Launch Time and/or Launch Date
         F6     Display MET & Launch Times     (now 2-Line Epoch Times)
         F7     Set FILENAMES and Paths
         F8     Set program TIME and/or DATE
         F9     DOS Shell             (CAUTION: DOS Version 3.x+ ONLY!)
         F10    Set STSORBIT PLUS Program Options and Features
         ENTER  Resume Mission                      (MIR Space Station)

         ESC    Quit STSORBIT PLUS and Save Current Mission

         Select desired function:

         WHILE MAP IS DISPLAYED:  F1 = HELP  ENTER = Main Menu

     During operation of STSPLUS, data are displayed by STSPLUS in several 
standard formats:

         4/05/1990       Date in month/day/year
          14:33:00 UTC   Coordinated Universal Time in hours:mins:secs
          06:33:00 PST   Local Time in hours:mins:secs (abbr. may vary)
        3/09:23:15       MET in days/hours:minutes:seconds
            320.50 nm    Distance in nautical miles
            551.37 km    Distance in kilometers
            -69.34       Angles in degrees; WEST longitude and SOUTH 
                         latitude are negative

Note that latitudes and longitudes also include "N" and "E" for positive 
values respectively, and "S" and "W" for negative values respectively. This 
convention, which may seem redundant, has been used to avoid possible 
confusion; there are a number of representations for latitude and longitude 
in common use which use different sign conventions. Azimuth (heading) is 
given in the sense North-East-South-West where North is 0 degrees, East is 
90 degrees, and so forth. The degree symbol is shown on the display for 
all angles but has been omitted from this documentation because it may not 
print correctly on all printers.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 59


F1     Convert Keplerian Data to 2-Line Format
----------------------------------------------

     This function provides a means to individuals without modems to 
receive the so-called "Keplerian Orbital Elements" by voice or other means 
and reliably convert those data to the "2-Line Element" format as required 
by STSPLUS and other satellite tracking programs. However, more data is 
included in the 2-line orbital element set than is usually distributed as 
the Keplerian orbital elements; this means that the missing data must 
either be obtained from other sources or be set to a specified value or 
zero. These instructions and the example and sample form which follows will 
help the unskilled user to do these tasks.
     This conversion function has but a single purpose: to prepare 2-line 
orbital elements from Keplerian orbital elements by means of user keyboard 
input. Since the program is designed only to transcribe valid data from one 
format to another, no error checking is performed and the program makes no 
tests of the "reasonableness" of the various data and parameters. The user 
is therefore cautioned to check his data before using this program, or to 
use the resulting data with caution until it has been verified.
     The information shown below is usually included in the Keplerian 
orbital elements as received via modem or voice (amateur radio or 
telephone). This sample is an actual file for Space Shuttle Flight STS-55 
launched in early 1993 as received via modem direct from the NASA Johnson 
Space Center prior to launch:

     Satellite: STS-55
     Catalog number: 00055
     Epoch time:      93073.67556033 =====> (14 MAR 93   16:12:48.41 UTC)
     Element set:     JSC-003
     Inclination:       28.4697 deg
     RA of node:       228.7025 deg          Space Shuttle Flight STS-55
     Eccentricity:     .0003812             Prelaunch Keplerian Elements
     Arg of perigee:   314.2100 deg         Launch:  14 MAR 93  15:00 UTC
     Mean anomaly:      45.8202 deg
     Mean motion:   15.90487610 rev/day              G. L. Carman
     Decay rate:     1.2020e-03 rev/day~2     NASA  Johnson Space Center
     Epoch rev:               2

     If you compare the information required by STSPLUS (as shown in the 
example on the following page) with that above, several items are missing 
or may be in a slightly different format. Here are some suggestions. 

1.   A sample form is included in this documentation which will assist you 
     when receiving Keplerian orbital information by voice or by amateur 
     radio link. Note that the form includes lines for "IAU Designation" 
     and "BSTAR Drag"; these items are frequently omitted and must be 
     determined independently (see below).

2.   The Catalog Number (often referred to as the NORAD Number) is assigned 
     by US Space Command at Cheyenne Mountain after a satellite has been 
     successfully launched. Initial or pre-launch Keplerian elements may 
     use the mission number or some other convenient number for this item. 
     Most tracking programs will accept any number here. STSPLUS uses the 
     Catalog number to keep track of launch date and time; if the Catalog
     number used for a mission changes, the launch date and time must be 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 60


     entered again.

3.   The Epoch time is the instant for which the Keplerial elements have 
     been calculated and is NOT the same as the launch date and time. 
     Launch date and time is shown separately, is NOT part of the 2-line 
     elements, and must be entered in STSPLUS using F5 from the Main Menu.

4.   The IAU (International Astronomical Union) Designation is often not 
     assigned until well after a flight is in progress; press ENTER to use 
     all spaces for this item.

5.   For the 2-line orbital element set, the element set number (shown as 
     "JSC-003" in the example above) MUST be numeric. For this example, 
     enter "3" or "003". Most tracking programs will accept any number for 
     this item, up to a maximum of FOUR DIGITS.

6.   The "Epoch Rev/Orbit" is the orbit number at the epoch (the instant 
     when the data is taken). Up to FOUR DIGITS may be entered here but 
     except for the orbit number on displays, this number has no effect on 
     the propagated orbit. NASA assigns Orbit/Rev 1 to the first partial 
     orbit following launch; US Space Command usually (but not always) 
     assigns Orbit/Rev 0 to the first partial orbit and the orbit number 
     for space shuttle missions must usually be adjusted to conform to NASA 
     convention.

7.   When the program asks for "NDOT2 Drag/Decay", the information being 
     requested is the "Decay rate" in the Keplerian elements. It may be 
     entered in the form shown in the example or as a decimal fraction such 
     as ".002102" (which is identical to the "2.10200e-03" in scientific 
     notation as used in the example).

8.   When the program asks for "NDDOT6 Drag", press ENTER to insert a value 
     of zero. This should be satisfactory for most satellites and most 
     tracking programs.

9.   When the program asks for "BSTAR", you may press ENTER to insert a 
     value of zero. This will be satisfactory for times very close to the 
     Epoch Time for the elements. However, as time progresses the satellite 
     may lag behind the propagated (projected) ground track if no value is 
     avaialble for BSTAR. For space shuttle missions, NASA often assigns a 
     default value of "25599-3" or ".00025599". A value from a prior set of 
     2-line elements may also be used.

10.  After all data have been entered, STSPLUS will request the filename to 
     which the 2-line orbital data is to be written. Enter the full 
     filename and filetype, such as "TESTSAT.TXT". The file will be written 
     to the drive and directory set using F7+F3 from the Main Menu. DO NOT 
     INCLUDE A DRIVE OR DIRECTORY; THAT IS ADDED AUTOMATICALLY! An existing 
     file with the same name will be overwritten.

11.  If you make a mistake during the data entry process, you may use the 
     BACKSPACE key until ENTER has been pressed. If you wish to cancel the 
     program without writing the data to a file, press ENTER when asked for 
     the filename and the data will be discarded.


Program STSORBIT PLUS Satellite Orbit Simulation                   Page 61


     As noted elsewhere, orbital elements have a limited lifetime. How long 
that lifetime may be depends primarily upon the orbital altitude. Low Earth 
orbit (LEO) satellites, especially those such as the space shuttle and 
Russian space station, are frequently maneuvered to maintain the desired 
orbit. Orbital elements for these satellites may be valid for only days or 
sometimes even hours. Orbital elements for higher orbital altitudes, say 
above 1,500 km, tend to be valid for much longer -- up to weeks. Satellites 
in very high or geosynchronous orbits exhibit usually long term orbital 
stability. The Bottom Line: The accuracy with which any tracking program 
can determine a satellite's position is primarily dependent upon having 
accurate orbital elements!
     Finally, a word about the NDOT2 and BSTAR parameters. A satellite's 
orbit is completely and accurately determined at the epoch time without 
NDOT2 and BSTAR. These two parameters determine various adjustments as the 
orbit is propagated in time and are a function of such things as orbital 
altitude, spacecraft attitude and cross-sectional area, atmospheric density 
changes due to sunspot activity, and so on. Both US Space Command and 
Johnson Space Center have been known to "tweak" these values for a variety 
of reasons, usually because the orbit is in a state of change due to 
maneuvers and/or excessive drag.
     NOTE: A positive exponent for BSTAR, which indicates high acceleration 
and is somewhat unusual (and often an indication of "tweaking"), is NOT 
handled correctly and must be manually edited. The resulting elements may 
not propagate accurately for more than a few hours.


EXAMPLE DATA INPUT
------------------

Enter 2-LINE ELEMENTS

Enter the required data as prompted. Most essential data is included in the 
Kelplerian Orbital Data available to amateur radio enthusiasts. Other data 
may be inserted if available or may be omitted if not. Accuracy may be 
affected, see documentation.

Enter Satellite Name (15 chars max):      sts-55
Enter NORAD Number (NNNNN):               55
Enter IAU Designation (8 chars max):
Enter Epoch Time (YYDDD.TTTTTTTT):        93073.67556033
Enter Element Set Number (NNN):           3
Enter Inclination (DDD.DDDD):             28.4697
Enter RA of Ascend Node (DDD.DDDD):       228.7025
Enter Eccentricity (.NNNNNNN):            .0003812
Enter Arg of Perigee (DDD.DDDD):          314.21
Enter Mean Anomaly (DDD.DDDD):            45.8202
Enter Mean Motion (NN.NNNNNNNN):          15.9048761
Enter Epoch Rev/Orbit (NNN):              2
Enter NDOT2 Drag/Decay (.NNNNNNNN):       .001202
Enter NDDOT6 Drag (NNNNN-N):              00000-0
Enter BSTAR (NNNNN-N):                    36300-3



Program STSORBIT PLUS Satellite Orbit Simulation                   Page 62


EXAMPLE DATA OUTPUT
-------------------

Satellite Data has been entered as:

Satellite Name (15 chars max):            Sts-55
NORAD Number (NNNNN):                     00055
IAU Designation (8 chars max):
Epoch Time (YYDDD.TTTTTTTT):              93073.67556033
Element Set Number (NNN):                  3
Inclination (DDD.DDDD):                    28.4697
RA of Ascend Node (DDD.DDDD):             228.7025
Eccentricity (.NNNNNNN):                  .0003812
Arg of Perigee (DDD.DDDD):                314.2100
Mean Anomaly (DDD.DDDD):                   45.8202
Mean Motion (NN.NNNNNNNN):                 15.90487610
Epoch Rev/Orbit (NNN):                     2
NDOT2 Drag/Decay (.NNNNNNNN):             .00120200
NDDOT6 Drag (NNNNN-N):                    00000-0
BSTAR (NNNNN-N):                          36300-3

Sts-55
1 00055U          93073.67556033  .00120200  00000-0  36300-3 0    33
2 00055  28.4697 228.7025 0003812 314.2100  45.8202 15.90487610    23

Enter FILENAME for 2-Line Elements:

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 63


RECEIVED KEPLERIAN ORBITAL DATA FORM
------------------------------------

     This form is provided as a convenience to users receiving Keplerian 
orbital data via voice link (amateur radio or telephone). Each set of 
underline characters indicates an expected character; the decimal point is 
shown where expected (if appropriate for the item). Make multiple copies of 
this form prior to a mission.


Satellite:          __ __ __ __ __ __ __ __ __ __ __ __ __ __ __


Catalog Number:     __ __ __ __ __


IAU Designation:    __ __ __ __ __ __ __ __
     

Epoch Time:         __ __ __ __ __ . __ __ __ __ __ __ __ __


Element Set:        __ __ __ __


Inclination:        __ __ __ . __ __ __ __


RA of Node:         __ __ __ . __ __ __ __


Eccentricity:       . __ __ __ __ __ __ __


Arg of Perigee:     __ __ __ . __ __ __ __


Mean Anomaly:       __ __ __ . __ __ __ __


Mean Motion:        __ __ . __ __ __ __ __ __ __ __


Decay Rate:         . __ __ __ __ __ __ __ __


BSTAR Drag:         __ __ __ __ __ - __


Epoch Rev:          __ __ __ __

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 64


F2     Read/Update NASA/NORAD 2-Line Elements from *.TXT/*.TLE Files
--------------------------------------------------------------------

     In order to read or update the NASA/NORAD 2-line elements, you must 
have a file with data for the appropriate satellites. A current file is 
included in the standard distribution of STSPLUS. These files have names 
such as "TLE239.TXT" where the "239" corresponds to the particular US Space 
Command Prediction Bulletin number from T. S. Kelso's Celestial BBS and may 
change several times per week. Other TLE files are available from my BBS.


     Update Current TDRS and Real Time Satellites
     --------------------------------------------

     Once TDRS and Real Time Satellites have been selected (using F6 from 
the Main Menu), it is necessary to periodically update the 2-line elements 
("TLEs") for these satellites so that the calculated positions are 
accurate. Naturally, this is also true for the primary satellite being 
tracked. TLEs have a limited lifetime. For higher altitude satellites such 
as geosynchronous satellites, 4 to 8 weeks is probably sufficient unless 
the satellite is being maneuvered (although I usually do this task at least 
weekly since I have the data). For low Earth orbit satellites, even when 
the satellite is not being maneuvered, I recommend a maximum interval 
between updates of 1 to 2 weeks; if the satellite is being maneuvered, such 
as is usually the case with the Space Shuttle, daily updates may be 
required.
     To update 2-line elements for the primary satellite and all TDRS and 
Real Time satellites, press F2 and select the desired file as described in 
the following section. Then enter the satellite name as "&" to request TLE 
update mode. The TLE file will be scanned and all satellite TLEs will be 
updated if their Epoch Time is later than those presently stored. The 
entire process takes only a few seconds. The following prompt illustrates 
the "Update" selection:

          Select NASA/NORAD 2-Line Elements File

          Enter 2-Line Filename  [GSFC267.TXT]:     GSFC267.TXT
          Enter Satellite Name/#nnnnn  [#20638]:    &
          (Enter '*' to match any satellite name, '&' for AUTO UPDATE)

As STSPLUS updates TLEs, a list of the satellites for which new TLEs have 
been loaded is displayed:

          Automatic TLE updates for:

          Satellite 3: Norad# 22314 @ 93217.59157166
          Satellite 2: Norad# 21639 @ 93219.36124578
          Satellite 8: Norad# 20580 @ 93218.03265951
          Satellite 1: Norad# 19883 @ 93220.90943044
          Satellite 4: Norad# 19548 @ 93220.44861278
          Satellite 6: Norad# 16609 @ 93220.81848976
          Satellite 5: Norad# 13969 @ 93220.48367176


          Press any key to continue ...

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 65



The satellite number indicates the "slot" in the TDRS and Real Time 
Satellite configuration, or "P" for the Primary Satellite. In the example 
shown, the TLEs for seven satellites were updated to the Epoch Times 
indicated. The updated TLEs will be saved in file STSPLUS.INI. Press ENTER 
to return to the Main Menu.


     Read NASA/NORAD 2-Line Elements from a File
     -------------------------------------------

     For both "Read" and "Update" functions, pressing F2 will display a 
list of all available files with default filetypes ".TXT" and ".TLE". The 
following example has been edited to show only 8 files:

     Select NASA/NORAD 2-Line Elements File

     Enter 2-Line Filename  [TLE147.TXT]:
     Use ARROW KEYS, press ENTER to use the current default file
     shown in square brackets [...], or press ESC to CANCEL.

      8 matching files in directory F:\TLE

     GPS.TXT
     GROUP000.TLE
     GSFC198.TXT
     GSFC199.TXT
     MIR.TLE
     TLE141.TXT
     TLE146.TXT
     TLE147.TXT

     The list of files is sorted in alphabetical order by filename then 
displayed using up to five columns. The display mode is adjusted for the 
maximum number of lines permissible for the active monitor type: 25 lines 
for CGA and HGC, 43 lines for EGA, and 50 lines for VGA. The maximum number 
of files which may be displayed for each monitor type is shown in the 
following table:

                    Screen     File      Max
          Monitor    Lines    Lines    Files
          ----------------------------------
          VGA           50       42      210
          EGA           43       35      175
          CGA/HGC       25       17       85

     To accept the default file shown in the square brackets, TLE147.TXT in 
the example, press ENTER. To manually enter a filename, type the name (the 
filetype .TXT will be appended if no filetype is typed) and press ENTER. To 
select one of the displayed files, use the ARROW KEYS (UP, DOWN, LEFT, 
RIGHT), Home, End, PgUp, or PgDn to move through the list until the desired 
file is highlighted and shown in the square brackets, then press ENTER. To 
cancel the function and return to the Main Menu, press ESC.
     STSPLUS defaults the drive and directory to the current directory, the 
one from which STSPLUS is being executed. However, some users prefer to use 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 66


a separate directory for 2-line elements files. To specify a different 
drive and/or directory, enter the drive (followed by a colon) and the 
desired directory (followed by a trailing backslash, "\"). The specified 
drive, directory, and filename are saved in file STSPLUS.INI and will be 
used the next time STSPLUS is executed. The following examples illustrate 
this method:

          D:\                 Use the root directory on drive D:

          \ELEMENTS\          Use the current drive and directory 
                              \ELEMENTS\

          C:\TLE\             Use drive C: and directory \TLE\

Failing to include the trailing backslash will cause STSPLUS to interpret 
what you intended as a directory to be a filename! The complete path with
filename and filetype mask may also be entered:

          C:\TLE\*.TXT        Use .TXT files on Drive C: and directory TLE

          D:\TLE\*.*          Display all files on drive D: and directory 
                              \TLE\

          F:\TLE\TLE*.TXT     Use drive F:, directory \TLE\ and all files 
                              matching "TLE*.TXT"

Although STSPLUS defaults to filetypes "*.TXT" and "*.TLE", you may use 
this command to temporarily specify a different filename and filetype mask 
if desired.
     If no files with filetype .TXT or .TLE (or files corresponding to the 
current filename and filetype mask) are found in the specified directory, 
the following error message will be displayed:

     No matching files found in specified drive/directory: E:\JUNK
     Press any key to continue ...

To specify NO fileltype, enter the filename followed by a period, i.e. 
"ELEMENTS.". Any desired filetype may be used, but the program will always 
default to ".TXT" and ".TLE" each time F2 is used.
     If you include a drive (such as "D:") and/or directory (the directory 
MUST be followed by a trailing backslash, "\"), and the drive or directory 
cannot be found, the following error message will be displayed:

     Drive or path error: E:\JUNK
     Press any key to continue ...

     Once the file has been selected, a default satellite name will appear 
in the next prompt:

     Enter 2-Line Filename  [STS50N38.TXT]:    STS50N38.TXT
     Enter Satellite Name/#nnnnn  [STS...]:
     (Enter '*' to match any satellite name, '&' for AUTO UPDATE)

     STSPLUS will normally display the first three characters of a 
satellite name or the full NORAD number, enclosed in square brackets, as 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 67


the default choice. If no prior satellite has been selected, the satellite 
name will default to "STS..." for space shuttle missions (provided the 
filename begins with "STS") and to "HST..." for all other satellites; 
otherwise, it will be the first three letters or full five digit NORAD 
number of the currently selected satellite. NORAD numbers are always 
prefixed with the "#" character. If you wish to change the information (or 
if no default is shown), enter the required information followed by ENTER. 
For the satellite name, only sufficient letters to unambiguously identify 
the desired satellite, upper or lower case, are required. For example, 
"Alou" would select "Alouette 1". However, note that entering "MIR" could 
select "MIRANDA" before it finds "MIR" depending upon the ordering of the 
2-line elements within the file. Alternatively, you may enter the NORAD 
number for the desired satellite by entering "#" followed by the number; 
leading zeroes may be omitted.
     Once the information has been entered, STSPLUS will attempt to locate 
the data for the requested satellite. If a satellite matching the requested 
name is found, the data for that satellite are displayed. Certain non-
essential data are not always included in the 2-line elements and may be 
replaced by spaces, indicated by "(n/a)".


     Satellite Name:              Mir
     Satellite NORAD Number:      #16609
     Elements File:               TLE233.TXT
     Elements File Record#:       315
                                  (*)
     Element Set Number:          201
     Elements Epoch:              93206.84472440
                                  25 JUL 1993 @ 20:16:24.188 UTC
     Orbit # at Epoch:            42516
     Launch Year:                 1986
     Launch Number:               17
     Launch Piece:                A
     Inclination:                 51.6213
     RA of Ascend Node:           25.384
     Eccentricity:                .0004375
     Arg of Perigee:              244.4461
     Mean Anomaly:                115.6366
     Mean Motion:                 15.58931226
     Acceleration/Drag:           .00007676
     BSTAR Drag:                  .000099999

     Press ENTER to ACCEPT this satellite, OR
     Press any other key to REJECT and continue searching:


     (*) This line is normally blank. However, one of the following 
     messages will appear here if a checksum error is detected in the 
     element set:

          BAD CHECKSUM in line 1 ignored!
          BAD CHECKSUM in line 2 ignored!
          BAD CHECKSUM in both lines ignored!

     In all three cases, STSPLUS will accept the data and attempt to use 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 68


     it. Be advised, however, that the checksums are included to help 
     detect data errors that might otherwise yield an incorrect position! 
     Serious errors may even cause STSPLUS to abort with an error message.

     For convenience, the Elements Epoch (the instant at which these 
orbital elements were calculated) is shown in two formats: the first format 
is that used in the 2-line elements, YYDDD.DDDDDDDD; and the second format 
is the same time converted into conventional date and time notation. You 
may thus see immediately how old the elements are and take this into 
account when evaluating the satellite's projected position.
     If this is the satellite you wish, press ENTER and the data will be 
entered into STSPLUS. If, on the other hand, a different satellite is 
desired, press any other key (such as the SPACE BAR) and STSPLUS will 
search for another name matching the requested satellite. For example, 
there are a number of NAVSTAR Global Positioning Satellites usually 
included in the file with official names such as "GPS-0001", "GPS-0002", 
"GPS BII-01" and so forth; requesting "GPS" will allow you to cycle through 
all the available choices. The file TLEnnn.TXT is an ASCII file; it may be 
helpful to view or print the file to see the available satellite names. 
     Once the satellite has been selected, STSPLUS will require a brief 
time to calculate certain required orbital parameters, then will proceed 
directly to the display of the ground track. However, if the current 
calculated altitude of the satellite is less than 75 nautical miles, the 
satellite has probably decayed. STSPLUS will display the following message 
before returning to the Main Menu:

         Satellite MIR DEB (#22209) indicates a current altitude less than
         75 nautical miles and has probably decayed. STSORBIT PLUS can NOT
         process the orbital data for this satellite!

         Use Function Key F2 from the Main Menu to select another
         satellite and verify the satellite NAME and NORAD NUMBER.

         Press any key to return to the Main Menu ...

     As a point of interest, the 2-line elements for the Space Shuttle 
Mission STS-50 used in the example above are as follows:

     STS-50
     1 22000U 92 34  A 92187.57342677 -.00032668  00000-0 -97874-4 0   380
     2 22000  28.4670 275.0700 0007237 340.7929  19.1530 15.91359642  1596


F3     Data Output and Pass Prediction Selections
-------------------------------------------------

     By popular request, STSPLUS has been enhanced to send selected data 
for the current satellite to other equipment via a serial port (COM1 or 
COM2), to a file (STSPLUS.LOG), or to the printer (LPT1). Validation of the 
serial port output has been accomplished using two computers and a "Null 
Modem" cable. Three classes of data may be selected for output: current 
position data in three formats, precision Earth-centered inertial ("ECI") 
state vectors in four formats, and tabular Line-of-Sight pass predictions
(which are also displayed on the screen). 
     The precision state vector outputs have been carefully coordinated 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 69


with Ken Ernandes so that they may be used as input to his program VEC2TLE, 
Version 9331 or later. Using these state vectors and VEC2TLE, the user may 
generate 2-line elements at any desired time (including just after the 
ascending node) for use with STSPLUS or other satellite tracking programs. 
With these programs, the user has a very powerful set of tools which can 
be used for a variety of analytical and display purposes. Cross validation 
of the two programs during Space Shuttle missions STS-56 and STS-55, as 
well as comparison with US Space Command data of comparable epoch, 
demonstrated high accuracy and excellent correlation.
     Each Data Output function is assigned a "Data Mode" number:

           1 = Azimuth, Elevation, Range
           2 = Latitude, Longitude, Orbit Altitude
           3 = Right Ascension, Declination
           4 = Ascending Node Data with State Vector
           5 = Precision X-Y-Z State Vector (2-Line Data)
           6 = Precision X-Y-Z State Vector (Comma Delimited)
           7 = Precision X-Y-X State Vector (Labeled Data)
           9 = Tabular Line-of-Sight Predictions

The current position data and precision state vectors are generated while 
the ground track map is displayed; for all Data Modes EXCEPT #4, data 
output may be logged continuously, for a specified time (UTC/GMT or local 
time), or for a specified time span (UTC/GMT or local time). Data Mode 4 
records data ONLY at the Ascending Node, e.g. when the Northbound equator 
crossing is detected. The predicted pass data is calculated "off-line" 
using UTC/GMT or local time, and is displayed on the screen as well as 
being sent to the selected output destination.

     Current position data include the UTC date/time and are generated for 
local horizon coordinates (altitude and azimuth), geographic coordinates 
(geocentric latitude, longitude, and orbital altitude), and topocentric 
equatorial coordinates (right ascension and declination calculated for the 
user's location). Precision X-Y-Z Earth-centered inertial state vectors 
(ECI position and velocity components) are generated as two numeric data 
lines, single line comma delimited, and multi-line labeled data. The 
details for each data output format are given in following sections.
     The precision ECI X-Y-Z state vectors, generated by STSPLUS for the 
true equator and equinox of date, have been extensively tested and 
validated in conjunction with Ken Ernandes' program VEC2TLE during Space 
Shuttle missions STS-56 and STS-55 in early 1993. For example, the 
combination of the two programs, STSPLUS and VEC2TLE, may be used to 
convert data between 2-line and ECI formats with very high accuracy. State 
vectors from STSPLUS may be read by VEC2TLE and converted into 2-line 
elements, then in turn read again by STSPLUS with essentially exact 
conversions. VEC2TLE has also been used during STS-56 and STS-55 to convert 
real time state vectors ("M50" or Mean of 1950) supplied courtesy Willie 
Musty of Mission Support, Rockwell International, into 2-line elements 
equal in accuracy to those generated by US Space Command (and made 
available four to eight hours sooner!). See the separate text section 
describing VEC2TLE.
     Note that the timing accuracy for Data Mode 4 is a fixed at 0.01 
seconds, regardless of the time step (X1, X10, or X60) then in effect. 
STSPLUS detects the Ascending Node data when the latitude switches from 
negative to positive on the Northbound crossing of the Equator. An 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 70


iterative process is then used to refine the time to the nearest 0.01 
seconds and the data at that time are recorded.
     Potential applications for the position data include automatic antenna 
pointing systems, off-line high precision plotting, and widespread 
distribution of the data within a large facility or via modem. ECI state 
vectors may be used in real time to create 2-line elements for a specified 
epoch to full precision. Users who develop applications to utilize these 
data are invited to contribute their programs and documentation for general 
use. Since these are new features for STSPLUS, comments and suggestions are 
welcome.

     Although STSPLUS retains the capability of performing off-line pass 
predictions with TS Kelso's TRAKSTAR or other satellite tracking software, 
many users have requested that a similar feature be incorporated directly 
into STSPLUS. Pass predictions may only be calculated for satellites having 
a mean motion greater than 1.5; this eliminates satellites in near 
geosynchronous or higher orbits, but since such satellites don't move much 
that does not represent a significant constraint. The satellite's orbit is 
examined for 48 hours, starting at the current real or simulated time, with 
a sampling interval which ranges from 10 to 60 seconds depending upon the 
orbit. Because of this "granularity" in the search algorithm, it is 
possible to skip passes whose duration is less than the sampling interval. 
Since those brief passes would barely peek above the user's horizon, they 
are thus not significant. Pass predictions may be continued in 48 hour 
segments until 99 passes have been displayed. Since a typical satellite may 
have from about two to seven passes in a 24 hour period, the passes may be 
examined for a considerable time into the future.
     Predicted pass data are calculated using the current satellite for 
Line-of-Sight visibility; that is, when the satellite is in line of sight 
to the user's location and without consideration of lighting effects. Since 
STSPLUS users are about equally divided between those who track satellites 
visually and those who use electronic equipment such as amateur radio, this 
method provides data for all users. Passes which occur near local sunrise 
or sunset may be tested for lighting constraints and/or ground visibility 
by displaying the ground track for the pass or other means. Dates and times 
may be displayed in Coordinated Universal Time (UTC/GMT) or in local time. 
Note that the date for each pass is given only for AOS (Acquisition of 
Signal); it is possible for the pass to span 00:00:00 hours (midnight) for 
the time scale in use with a consequent date change during the pass for MAX 
VISIBILITY and/or LOS (Loss of Signal).
     Prediction calculations may require some time; calculation delays are 
noted with the message "calculating ...". Using a processor equipped with a 
math coprocessor chip, each 48 hour block may require from less than 10 
seconds to a minute or more. However, users without math coprocessor chips 
will experience significant delays -- minutes or even tens of minutes! The 
following table lists typical calculation times for various processors (all 
with math coprocessors!) using the Russian MIR Space Station:

                    286/287        386SX/387SX         486DX
                    8 MHz          20 MHz              33 MHz
          ---------------------------------------------------     
          MIR       60 sec         30 sec              6 sec

     The data output feature MUST be enabled with F3 each time STSPLUS is 
run; it is NOT automatically restarted when the "/R" (RESUME) command line 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 71


option is used.

                              **********
                              *  NOTE  *
                              **********

     Users are reminded that when data output is sent to the file 
     STSPLUS.LOG, a considerable volume of data may be accumulated 
     over long periods of time. It is possible to completely fill a 
     disk with this data! The file should be periodically copied to 
     other media or deleted to avoid this problem.


Setting Up Position and State Vector Data Output
------------------------------------------------

     Data output of position and state vectors ONLY occurs while the 
ground track is displayed; no data are generated until the ground track is 
actually in progress! The appropriate data are sent to the destination 
device at the selected data interval (continuous), at a specified time, or 
at the selected data interval over a specified time span covering no more 
than 24 hours.


                         ************************
                         *  IMPORTANT REMINDER  *
                         ************************

     STSPLUS generates Earth-Centered Inertial ("ECI") state vectors 
     for the true equator and equinox of date. Other software and 
     various agencies may use different coordinate systems. In 
     particular, NASA uses the mean equator and equinox of the 
     Besselian year 1950 ("Mean of 1950", "M50" or "B1950"). 
     Astronomers and other agencies may use the mean equator and 
     equinox of the Julian year 2000 ("Mean of 2000" or "J2000"). 
     Other agencies, such as the DOD C-Band Radar Network, use a time-
     independent coordinate system ("Earth-fixed Greenwich" or "EFG") 
     for predicted state vectors prior to a launch. Users must take 
     care that the appropriate coordinate system is used for each 
     application and/or perform the required conversions.


     STSPLUS sets up certain initial default parameters for data output and 
displays the current parameters each time F3 is pressed, as shown in the 
following example:

         STSORBIT PLUS Data Output Parameters:

         Data Output:                  STSPLUS.LOG

         Data Format:                  7 = Precision X-Y-Z State Vector
         Data Interval:                60 seconds (continuous)
         Data Units:                   Kilometers, Multi-Line Labeled
         Accept Parameters [Y,n,x]:


Program STSORBIT PLUS Satellite Orbit Simulation                   Page 72


     To cancel data output and return to the Main Menu, press "X". If the 
current parameters are correct, press "Y" (or ENTER) to accept them. If the 
parameters are to be changed or if a specified time or time span is 
desired, press "N" to be prompted for new parameters. In each case, the 
default value which will be used if ENTER is pressed will be shown in 
square brackets; if more than one choice is shown, separated by commas, the 
first choice will be used if ENTER is pressed. The user must first select 
the data output device or destination by pressing the indicated key:

         Select Output [F,p,1,2]:
           F = File STSPLUS.LOG
           P = Printer LPT1:
           1 = Serial Port COM1:
           2 = Serial Port COM2:

Pressing ENTER or the letter "F" (upper or lower case) will select the FILE 
output and the data will be sent to the file STSPLUS.LOG. If the file does 
not exist, it will be created; if the file already exists, the data will be 
appended to the existing data. Press the letter "P" to direct the data to 
the printer on LPT1. Press "1" or "2" to direct the data to one of the two 
serial ports.
     When a serial port (COM1: or COM2:) is selected, the user next selects 
the data rate to be used for communications with the external equipment. 
Only the four data rates shown below the prompt are supported. Use the 
first character of the desired rate to select it, or press ENTER to use the 
data rate shown in the square brackets:

         Select DATA RATE [9600]:
         (300, 1200, 2400, 9600)

STSPLUS automatically sets the communications parameters to "8,N,1"; these 
are fixed and may not be altered. These communications parameters select 8 
data bits per transmitted byte, NO parity, and 1 stop bit. Most external 
equipment will operate satisfactorily with these parameters. 
     STSPLUS requires several additional items of information before it can 
send data to the external equipment, file or printer. The first is the data 
format to be used. Eight different data formats are available. The next 
prompt lists the formats and shows the current default in square brackets:

         Select Data to Output [7]:
           1 = Azimuth, Elevation, Range
           2 = Latitude, Longitude, Orbit Altitude
           3 = Right Ascension, Declination
           4 = Ascending Node X-Y-Z State Vector
           5 = Precision X-Y-Z State Vector (2-Line Data)
           6 = Precision X-Y-Z State Vector (Comma Delimited)
           7 = Precision X-Y-X State Vector (Labeled Data)
           9 = Tabular Line-of-Sight Predictions

Press the number key corresponding to the desired Data Mode or press ENTER 
to select the choice shown in square brackets. See the Data Mode Formats in 
the following sections for specific details on the data included in each 
data mode.
     For current position and state vector formats except Data Mode 4, the 
desired time interval between successive sets of data must be also 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 73


selected. (Data Mode 4 records data immediately after the Ascending Node 
and does not use the time interval parameter.) Any interval between 1 and 
900 seconds may be selected (that is, up to 15 minutes maximum). Add the 
letter "T" or "t" if you wish the data to be logged for a specific time or 
time span. Note also that this is the DESIRED time interval; if your 
computer is too slow to complete its calculations in that time, the 
interval will be longer. In other words, STSPLUS will generate the 
requested data no more frequently than the interval requested but may take 
longer, depending upon what has to be done each time. In response to the 
prompt, press ENTER to accept the default value shown in square brackets or 
type the desired numerical value (in seconds) followed by ENTER:

         Data Interval (secs) [60]:
           (Min = 1 sec, Max = 900 secs; Add 'T' for timer)

If a value less than 1 second is entered, 1 second will be substituted; if 
a value greater than 900 seconds is entered, 900 will be substituted. If 
"T" is entered by itself, the default value shown in square brackets will 
be used for the Data Interval.
     If "T" is appended to the desired interval or is entered by itself, 
STSPLUS requests the Start Time for logging:

         Start Time (HH:MM:SS):
           (Add 'U' or 'G' for UTC/GMT)

Enter the desired LOCAL Start Time or add the letter "U" or "G" for UTC/GMT 
time. STSPLUS will reformat the entered time and add the appropriate time 
zone designation, then prompt for the Stop Time:

         Start Time (HH:MM:SS):        08:45:00 PDT
         Stop Time (HH:MM:SS):
           (Press ENTER for Stop Time = Start Time)

Enter the desired Stop Time using the SAME time scale used for Start Time, 
or press ENTER to use the Start Time. STSPLUS will reformat the entered 
time and add the appropriate time zone designation.

         Stop Time (HH:MM:SS):         08:50:00 PDT

When Start Time equals Stop Time, only one set of data will be recorded. 
Reasonable care is required when setting up these times. If the current 
time (real or simulated) is past the Start Time, data will be recorded 
immediately. Times may be set to less than 24 hours into the future.
     When state vectors are requested (Data Modes 5 through 7), STSPLUS 
must also know the desired units of measure, kilometers ("km" or "KM"), 
feet ("ft" or "FT"), or nautical miles ("nm" or "NM"):

         Data Units [KM,ft,nm]:
           (Press 1st letter to select)

Press the first letter of the desired units of measure or press ENTER for 
the current default units of measure (shown in capital letters in the 
prompt, "KM" in the example above).
     STSPLUS now displays the new parameters for approval:


Program STSORBIT PLUS Satellite Orbit Simulation                   Page 74


         STSORBIT PLUS Data Output Parameters:

         Data Output:                  STSPLUS.LOG

         Data Format:                  7 = Precision X-Y-Z State Vector
         Data Interval:                60 seconds, 08:45:00-08:50:00 PDT
         Data Units:                   Kilometers, Multi-Line Labeled
         Accept Parameters [Y,n,x]:

If no Start and Stop Times have been entered, "(continuous)" will appear in 
place of the Start and Stop Times.
     As before, press "Y" (or ENTER) to accept the parameters and enable 
data output, "N" to re-enter the parameters, or "X" to cancel data output 
and return to the Main Menu.


Setting Up Tabular Pass Predictions
-----------------------------------

     Tabulation of predicted passes is always displayed on the screen and 
may optionally be sent to a destination device. The appropriate data are 
displayed and sent to the destination device at the selected data interval 
(continuous), at a specified time, or over a specified time span covering 
no more than 24 hours.
     STSPLUS sets up certain initial default parameters for tabular pass 
predictions and displays the current parameters each time F3 is pressed, as 
shown in the following example:

         STSORBIT PLUS Data Output Parameters:

         Data Output:                  STSPLUS.LOG

         Data Format:                  9 = Tabular Line-of-Sight Predictions
                                           (Using PDT for times)

         Accept Parameters [Y,n,x]:

     To cancel data output and generate pass predictions on the screen 
ONLY, press "X". If the current parameters are correct, press "Y" (or 
ENTER) to accept them. If the parameters are to be changed or if a 
specified time is desired, press "N" to be prompted for new parameters. In 
each case, the default value which will be used if ENTER is pressed will be 
shown in square brackets; if more than one choice is shown, separated by 
commas, the first choice will be used if ENTER is pressed. The user must 
first select the data output device or destination by pressing the 
indicated key:

         Select Output [F,p,1,2]:
           F = File STSPLUS.LOG
           P = Printer LPT1:
           1 = Serial Port COM1:
           2 = Serial Port COM2:

Pressing ENTER or the letter "F" (upper or lower case) will select the FILE 
output and the data will be sent to the file STSPLUS.LOG. If the file does 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 75


not exist, it will be created; if the file already exists, the data will be 
appended to the existing data. Press the letter "P" to direct the data to 
the printer on LPT1. Press "1" or "2" to direct the data to one of the two 
serial ports.
     When a serial port (COM1: or COM2:) is selected, the user next selects 
the data rate to be used for communications with the external equipment. 
Only the four data rates shown below the prompt are supported. Use the 
first character of the desired rate to select it, or press ENTER to use the 
data rate shown in the square brackets:

         Select DATA RATE [9600]:
         (300, 1200, 2400, 9600)

STSPLUS automatically sets the communications parameters to "8,N,1"; these 
are fixed and may not be altered. These communications parameters select 8 
data bits per transmitted byte, NO parity, and 1 stop bit. Most external 
equipment will operate satisfactorily with these parameters. 
     STSPLUS requires several additional items of information before it can 
send data to the external equipment, file or printer. The first is the data 
format to be used. Five different data formats are available. The next 
prompt lists the formats and shows the current default in square brackets:

         Select Data to Output [7]:
           1 = Azimuth, Elevation, Range
           2 = Latitude, Longitude, Orbit Altitude
           3 = Right Ascension, Declination
           4 = Ascending Node X-Y-Z State Vector
           5 = Precision X-Y-Z State Vector (2-Line Data)
           6 = Precision X-Y-Z State Vector (Comma Delimited)
           7 = Precision X-Y-X State Vector (Labeled Data)
           9 = Tabular Line-of-Sight Predictions

Press the "9" number key to select tabular pass predictions or press ENTER 
to select the choice shown in square brackets. See the Data Mode Formats in 
the following sections for specific details on the data included in each 
data mode.
     For tabular line-of-sight predictions, STSPLUS must know the time zone 
for which data is to be displayed. The choices are UTC/GMT or the LOCAL 
time zone:

         Use UTC or PDT time [PDT]:
           (Use LEFT LETTER of abbreviation to select);

Depending upon the user's choice when the UTCOffset was set, either "UTC" 
or "GMT" will be displayed along with the abbreviation for the local time 
zone. Use the left-most letter of the desired time zone, or press ENTER to 
accept the time zone shown in the square brackets ("[PDT]" in the example).
     STSPLUS now returns to the initial parameter display and again asks if 
the parameters are correct. As before, press "Y" to proceed with pass 
predictions AND sending the data to the specified destination device, "N" 
to change parameters, or "X" return to the Main Menu and display the pass 
predictions on the screen WITHOUT sending the data to a destination device.
     For tabular Line-of-Sight predictions, the data are displayed on the 
screen as calculated and optionally sent to the selected destination 
device. The following is an edited sample of the screen display:

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 76



   ---------16609 AOS--------  ---MAX VISIBILITY--  ------LOS------
 #   UTC Date UTC Time    Azm  UTC Time Alt    Azm  UTC Time    Azm Duration
 1 02/23/1993 03:05:56  171.5  03:09:39   7  125.1  03:13:23   78.4  0:07:27
 2 02/23/1993 04:40:12  230.2  04:45:23  70  318.8  04:50:32   44.9  0:10:20
 3 02/23/1993 06:17:58  281.3  06:22:02   9  333.9  06:26:07   26.7  0:08:09
 4 02/23/1993 07:57:27  328.5  07:59:40   2  354.4  08:01:53   20.3  0:04:26
 5 02/23/1993 09:34:31  339.1  09:37:34   4   15.9  09:40:38   52.7  0:06:07
 6 02/23/1993 11:09:57  325.6  11:14:46  21   34.8  11:19:35  103.4  0:09:38
 7 02/23/1993 12:46:00  302.3  12:50:56  29  229.0  12:55:55  155.6  0:09:55
 8 02/24/1993 02:12:22  131.7  02:13:17   0  121.3  02:14:12  110.9  0:01:50
 9 02/24/1993 03:43:39  212.0  03:48:44  42  132.6  03:53:48   53.7  0:10:09
10 02/24/1993 05:20:25  263.7  05:25:02  16  327.6  05:29:40   31.9  0:09:15
11 02/24/1993 06:59:36  314.0  07:02:22   3  347.0  07:05:09   20.0  0:05:33
12 02/24/1993 08:37:54  340.4  08:40:18   2    8.7  08:42:43   37.0  0:04:49
13 02/24/1993 10:13:30  331.3  10:17:49  12   28.7  10:22:09   85.8  0:08:39
14 02/24/1993 11:49:11  311.8  11:54:20  79  224.7  11:59:31  137.0  0:10:20
15 02/24/1993 13:26:53  273.2  13:29:57   4  236.4  13:33:01  199.8  0:06:08
Elapsed time = 27 seconds
Repeat for NEXT 48 HOURS or DISPLAY PASS [N,y,pass#]:

The column headings indicate the data displayed. "16609" indicates that the 
data is for NORAD number 16609, the MIR Space Station. "AOS" is Acquisition 
of Signal or when the satellite rises above the user's true horizon. "MAX 
VISIBILITY" is the maximum altitude above the user's true horizon that the 
satellite reaches during the pass. "LOS" is Loss of Signal or when the 
satellite sets below the user's true horizon. "#" is an arbitrary pass 
number for this set of calculations. The format for the data sent to the 
destination device is slightly different from that displayed; see the Data 
Mode 9 format description below.
     The user may select either UTC/GMT or LOCAL date and times for pass 
predictions. If other than UTC is selected, substitute the appropriate time 
zone abbreviation as required. The date is given only for AOS; since passes 
may span 00:00:00 hours for the selected time zone, the actual date for MAX 
VISIBILITY and/or LOS may have to be incremented.
     Times are calculated to the nearest second, altitudes are rounded to 
the nearest degree, and azimuths are rounded to the nearest tenth of a 
degree. Azimuth is always calculated in the sense NESW where North = 0 
degrees, West = 90 degrees, etc. Note that the degree symbol will appear on 
the display for all "Azm" and "Alt" data but has been deleted in the sample 
above in order to maintain compatibility with various printers; the actual 
display is thus four columns wider than the example above.
     Press ENTER while the passes are being calculated to stop the 
calculations. When all calculations for the current 48 hour block have been 
completed, the time elapsed for the calculations is displayed and the user 
is asked if another set of calculations is desired of if a particular pass 
should be displayed. Press "N" or ENTER to return to the Main Menu, or 
press "Y" to perform the next 48 hour block of calculations. The 
calculations will be stopped when 99 passes have been listed. Typically, 
from four to sixteen passes are listed for each 48 hour block, the number 
being related to the characteristics of the current satellite's orbit. If 
additional passes beyond that time are desired, set simulated time (F8+F3 
from the Main Menu) to the desired start time and repeat the predictions.
     To display a particular pass, enter the listed pass number. Passes are 
assigned arbitrary numbers from 1 to 99 beginning with the first pass which 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 77


occurs during or subsequent to the current real or simulated time. Any pass 
number may be selected, from pass #1 to the last listed pass shown on the 
screen. (Attempting to enter a pass number larger than the last one shown 
will cause the computer to "beep" and the prompt will be repeated.) STSPLUS 
will set simulated time to approximately 30 seconds prior to the mid-point 
of the selected pass and prepare the display. The pass may then be examined 
for details of lighting, ground track, and so forth. STSPLUS displays "VIS" 
next to the orbit inclination if a visual sighting may be possible. While 
examining the pass, use F6 to PAUSE the display, then use the "+" or "-" 
keys to adjust the simulated time forward or backward. The default time 
step is one second; press F4 to select a different time step: 1, 10, or 60 
seconds. Press ENTER to return to normal operation from the PAUSE mode.
     Each time predicted passes are requested, the list begins with the 
first pass which occurs at or subsequent to the current real or simulated 
time. Note that STSPLUS automatically sets simulated time to display a 
predicted pass, and that new simulated time remains in effect until the 
user returns to the Main Menu, at which point the time is restored to the 
real or simulated time in effect BEFORE the pass prediction was displayed. 
Repeated use of pass predictions will therefore generally produce the same 
list of passes; however, if sufficient time elapses between predictions 
that a pass "comes and goes", new pass numbers will be displayed.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 78


Data Mode 1: Azimuth/Elevation Data Format
------------------------------------------

          1         2         3         4         5
0123456789012345678901234567890123456789012345678901234
-------------------------------------------------------
02/10/1993  13:58:09  20580    -2.472   248.222    1675 [CR/LF]
-----+----  ----+---  --+--  ----+---  ----+--- ---+---
     |          |       |        |         |       |
     |          |       |        |         |       +--- Range 
     |          |       |        |         |
     |          |       |        |         +----------- Aximuth
     |          |       |        |
     |          |       |        +--------------------- Elevation
     |          |       |
     |          |       +------------------------------ NORAD #
     |          |
     |          +-------------------------------------- UTC Time
     |
     +------------------------------------------------- UTC Date


UTC Date:      Current date in Universal Coordinated Time, mm/dd/yyyy

UTC Time:      Current time in Universal Coordinated Time, hh:mm:ss

NORAD #:       Satellite NORAD Number

Azimuth:       Azimuth in degrees to satellite in the sense NESW

Elevation:     Elevation to satellite in degrees above true horizon

Range:         Range from User Location to Satellite in km

[CR/LF]:       Each data line is terminated with a CR and LF in addition to 
               the 54 printing characters shown, for a total of 56 
               characters per data line.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 79


Data Mode 2: Latitude/Longitude Data Format
-------------------------------------------

          1         2         3         4         5
0123456789012345678901234567890123456789012345678901234
-------------------------------------------------------
02/11/1993  13:46:40  20580    -5.182   155.667     593 [CR/LF]
-----+----  ----+---  --+--  ----+---  ----+--- ---+---
     |          |       |        |         |       |
     |          |       |        |         |       +--- Orbit Altitude
     |          |       |        |         |
     |          |       |        |         +----------- Longitude
     |          |       |        |
     |          |       |        +--------------------- Latitude
     |          |       |
     |          |       +------------------------------ NORAD #
     |          |
     |          +-------------------------------------- UTC Time
     |
     +------------------------------------------------- UTC Date


UTC Date:      Current date in Universal Coordinated Time, mm/dd/yyyy

UTC Time:      Current time in Universal Coordinated Time, hh:mm:ss

NORAD #:       Satellite NORAD Number

Latitude:      Geodetic Latitude in degrees of sub-satellite point 
               (satellite ground track)

Longitude:     Geodetic Longitude in degrees of sub-satellite point 
               (satellite ground track)

Orbit Alt:     Altitude in kilometers of the satellite above the Earth's 
               surface 

[CR/LF]:       Each data line is terminated with a CR and LF in addition to 
               the 54 printing characters shown, for a total of 56 
               characters per data line.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 80


Data Mode 3: Topocentric RA/DEC Data Format
-------------------------------------------

          1         2         3         4
01234567890123456789012345678901234567890123456
-----------------------------------------------
02/11/1993  13:47:20  20580     7.111   -25.941 [CR/LF]
-----+----  ----+---  --+--  ----+---  ----+---
     |          |       |        |         |
     |          |       |        |         +----------- DEC
     |          |       |        |
     |          |       |        +--------------------- RA
     |          |       |
     |          |       +------------------------------ NORAD #
     |          |
     |          +-------------------------------------- UTC Time
     |
     +------------------------------------------------- UTC Date


UTC Date:      Current date in Universal Coordinated Time, mm/dd/yyyy

UTC Time:      Current time in Universal Coordinated Time, hh:mm:ss

NORAD #:       Satellite NORAD Number

RA:            Topocentric Right Ascension in hours

DEC:           Topocentric Declination in degrees

[CR/LF]:       Each data line is terminated with a CR and LF in addition to 
               the 46 printing characters shown, for a total of 48 
               characters per data line.

NOTES:

1.   Topocentric coordinates give the right ascension and declination as 
     seen from the current user's location on the surface of the Earth.

2.   Coordinates are equator and equinox of date.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 81


Data Mode 4: Ascending Node X-Y-X State Vector
----------------------------------------------

STSORBIT PLUS Data Output to STSPLUS.LOG, Data = 4 
Satellite Name:         MIR Space Station
Catalog Number:         16609  86 17  A
Epoch Date/Time:        93206.71622934028
                        07/25/1993  17:11:22.215 UTC
ECI X:                   6083.74442210995 km
    Y:                   2969.71930867257 km
    Z:                      0.01043524694 km
    Xdot:                  -2.09290827983 km/sec
    Ydot:                   4.27922666083 km/sec
    Zdot:                   6.01892329735 km/sec
Ndot/2 (Drag):              0.00056174000
Nndot/6:                    0.00000000000
B-Star:                     0.00071196000
ElSet #:                  196.00000000000
Rev @ Epoch:            42514.00433526011


STSORBIT PLUS Data Output to STSPLUS.LOG, Data = 14 
Satellite Name:         MIR Space Station
Catalog Number:         16609  86 17  A
Epoch Date/Time:        93206.71622934028
                        07/25/1993  17:11:22.215 UTC
ECI X:               19959752.12027331000 ft
    Y:                9743154.40544174400 ft
    Z:                     34.23630116129 ft
    Xdot:               -6866.48346437341 ft/sec
    Ydot:               14039.42991197058 ft/sec
    Zdot:               19747.08480675116 ft/sec
Ndot/2 (Drag):              0.00056174000
Nndot/6:                    0.00000000000
B-Star:                     0.00071196000
ElSet #:                  196.00000000000
Rev @ Epoch:            42514.00523843931


STSORBIT PLUS Data Output to STSPLUS.LOG, Data = 24 
Satellite Name:         MIR Space Station
Catalog Number:         16609  86 17  A
Epoch Date/Time:        93206.71622934028
                        07/25/1993  17:11:22.215 UTC
ECI X:                   3284.95919120368 nm
    Y:                   1603.52014507239 nm
    Z:                      0.00563458372 nm
    Xdot:                  -1.13008006471 nm/sec
    Ydot:                   2.31059754904 nm/sec
    Zdot:                   3.24995858388 nm/sec
Ndot/2 (Drag):              0.00056174000
Nndot/6:                    0.00000000000
B-Star:                     0.00071196000
ElSet #:                  196.00000000000
Rev @ Epoch:            42514.00325144509

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 82


NOTES:

1.   The X-Y-Z Cartesian State Vector is given as a standard Earth-centered 
     inertial ("ECI") cartesian 6-dimensional state vector where the X-Axis 
     is pointing toward the vernal equinox, the Z-Axis is pointing toward 
     the North Pole, and the Y-Axis is mutually orthogonal to the other 
     axes in a right-handed axis system. All coordinates are for true 
     equator and equinox of date.

2.   The units of measure for the state vector may be determined by the 
     tens digit of the Data Mode in the initial header line as well as 
     being indicated with the data:

      4   Kilometers and kilometers per second
     14   Feet and feet per second
     24   Nautical miles and nautical miles per second

3.   One data item is given per line, labeled as shown in the examples. The 
     data in the first four lines (Satellite Name, Catalog Number, and two 
     lines of Date/Time) begin in column 25. The remaining numeric data 
     items begin in column 21 and use a FORTRAN-like format statement 
     F21.11.

4.   The Catalog Number is given first as the NORAD Number ("16609" in the 
     example) and then as the IAU Designation ("86 17  A"). The IAU 
     Designation is separated from the NORAD Number by two spaces. Some 2-
     line elements omit the IAU Designation, in which case that portion 
     will be blank.

5.   Note that the Date/Time is presented on two lines in two different 
     formats. The first format is the NASA Day-of-Year ("DOY") format, 
     YYDDD.DDDDDD, since that is the format used by NASA/JSC for X-Y-Z 
     state vectors for the Space Shuttle, in 2-line elements, and in 
     program VEC2TLE. In the DOY format, time is counted from midnight 
     (00:00 UTC) each day. Some calculations may require instead the Julian 
     Date format which counts time from noon (12:00 UTC) each day. The 
     Date/Time is also "decoded" and given in the more conventional 
     "MM/DD/YYYY  HH/MM/SS.SSS" format for clarity using Coordinated 
     Universal Time (UTC/GMT).

6.   The ElSet Number is specified in the 2-line elements used to generate 
     the ground track and is always given as an integer. Note that ElSet 
     Numbers may not necessarily follow in sequence and that different 
     sources will use different sequences of ElSet numbers.

7.   The Rev Number at Epoch (the orbit number at the time the data is 
     sampled) is based upon the Rev Number specified in the 2-line elements 
     used to generate the ground track. The fractional part is calculated 
     by STSPLUS geometrically from the ascending node. Note that US Space 
     Command uses a different orbit numbering convention than does NASA for 
     space shuttle missions; US Space Command usually specifies the first 
     (partial) orbit number as Rev 0, while NASA specifies that orbit 
     number as Rev 1. For satellites which have been in orbit for long 
     periods of time, the Rev Number may be arbitrary.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 83


Data Mode 5: Precision X-Y-Z Cartesian State Vector, 2 Data Lines
-----------------------------------------------------------------

STSORBIT PLUS Data Output to STSPLUS.LOG, Data = 5 
20580  93110.043125      4920.98348         4440.02814        -2158.84295
                           -4.02147461570      5.78870948196      2.74131815428
20580  93110.043171      4904.85124         4463.14112        -2147.85724
                           -4.04461763461      5.76773962933      2.75148946765

STSORBIT PLUS Data Output to STSPLUS.LOG, Data = 15 
20580  93110.045081  13656864.66720     17514322.54968     -5452252.42794
                       -16168.27686974290  15789.75251859515  10248.33566657315
20580  93110.045139  13575822.39276     17593013.13238     -5400930.14914
                       -16248.48336702945  15686.35334359047  10280.38786725583

STSORBIT PLUS Data Output to STSPLUS.LOG, Data = 25 
20580  93110.046829      1817.50246         3234.50460         -631.72242
                           -3.02340746009      2.05326951871      1.82336359537
20580  93110.046991      1774.96638         3262.87575         -606.12299
                           -3.05304428709      1.99966800523      1.83360328215

NOTES:

1.   The X-Y-Z Cartesian State Vector is given as a standard Earth-centered 
     inertial ("ECI") cartesian 6-dimensional state vector where the X-Axis 
     is pointing toward the vernal equinox, the Z-Axis is pointing toward 
     the North Pole, and the Y-Axis is mutually orthogonal to the other 
     axes in a right-handed axis system. All coordinates are for true 
     equator and equinox of date.

2.   The units of measure for the state vector may be determined by the 
     tens digit of the Data Mode in the initial header line:

      5   Kilometers and kilometers per second
     15   Feet and feet per second
     25   Nautical miles and nautical miles per second

3.   The NASA Day-of-Year format is used here for date and time since that 
     is the format used by JSC for X-Y-Z state vectors and also in 2-line 
     elements. In the DOY format, time is counted from midnight (00:00 UTC) 
     each day. Some calculations may require instead the Julian Date format 
     which counts time from noon (12:00 UTC) each day.

4.   Two successive data samples are shown for each data mode.

5.   The following FORTRAN-like format statements may be used to read the 
     two lines of data in this mode for all units of measure:

     First Line:
     -----------
          Catalog #:     I5
                         2X
          Date/Time:     F15.9
          X:             F15.5
                         4X

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 84


          Y:             F15.5
                         4X
          Z:             F15.5
                         CR/LF

     Second Line:
     ------------
                         23X
          Xdot:          F18.11
                         1X
          Ydot:          F18.11
                         1X
          Zdot:          F18.11
                         CR/LF

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 85


Data Mode 6: Precision X-Y-Z Cartesian State Vector, Comma Delimited
--------------------------------------------------------------------

STSORBIT PLUS Data Output to STSPLUS.LOG, Data = 6 
0,0,20580,93110.0476041667,2982.28779295502,6229.01725815628,-940.796339818487,
                           -5.85010701911522,3.3199940892324,3.46047048985284
0,0,20580,93110.0476851852,2941.25120957693,6252.07713790904,-916.54588610151,
                           -5.87454395677527,3.2685046500327,3.46815363454982

STSORBIT PLUS Data Output to STSPLUS.LOG, Data = 16 
0,1,20580,93110.0482060185,8771281.06140276,20969911.6226162,-2491608.1429704,
                           -19762.0576284838,9623.02409449012,11524.6952898439
0,1,20580,93110.0482638889,8672341.7437806,21017717.5456987,-2433947.77946384,
                           -19813.4647395816,9499.28476766938,11539.2506632381

STSORBIT PLUS Data Output to STSPLUS.LOG, Data = 26 
0,2,20580,93110.0493865741,1103.65585656622,3591.279279101,-214.476932551084,
                           -3.4057330597861,1.1598790254898,1.9344163566285
0,2,20580,93110.049537037,1059.27271053518,3605.99939807939,-189.308779132495,
                           -3.42231018081901,1.10471766926502,1.93751948609809

NOTES:

1.   The X-Y-Z Cartesian State Vector is given as a standard Earth-centered 
     inertial ("ECI") cartesian 6-dimensional state vector where the X-Axis 
     is pointing toward the vernal equinox, the Z-Axis is pointing toward 
     the North Pole, and the Y-Axis is mutually orthogonal to the other 
     axes in a right-handed axis system. All coordinates are for true 
     equator and equinox of date.

2.   The units of measure for the state vector may be determined by the 
     tens digit of the Data Mode in the initial header line as well as the 
     second parameter in the comma delimited data string:

     Data Param
     Mode    #2     Units
     -----------------------------------------------------------
        6     0     Kilometers and kilometers per second
       16     1     Feet and feet per second
       26     2     Nautical miles and nautical miles per second

3.   The comma delimited data are generated as a single line terminated by 
     CR/LF. The examples above have been split into two lines for printing 
     purposes.

4.   The data are written in a single data line in the following order, 
     separated by a comma between items:

     Epoch Flag, always zero signifying equator and equinox of date.
     Units Flag (see Note 1 above)
     Catalog/NORAD number
     Date (YYDDD.DDDDDDDD... format)
     ECI X
     ECI Y
     ECI Z

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 86


     ECI Xdot
     ECI Ydot
     ECI Zdot

5.   Line length will vary as a function of the data.

6.   Two successive data samples are shown for each data mode.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 87


Data Mode 7: Precision X-Y-Z Cartesian State Vector, Labeled Data
-----------------------------------------------------------------

STSORBIT PLUS Data Output to STSPLUS.LOG, Data = 7 
Satellite Name:         MIR Space Station
Catalog Number:         16609  86 17  A
Epoch Date/Time:        93192.11956018518
                        07/11/1993  02:52:10.000 UTC
ECI X:                  -3441.20195444797 km
    Y:                  -3110.29870646026 km
    Z:                   4920.32069520120 km
    Xdot:                   2.90216455238 km/sec
    Ydot:                  -6.74909064951 km/sec
    Zdot:                  -2.23710677970 km/sec
Ndot/2 (Drag):              0.00008567000
Nndot/6:                    0.00000000000
B-Star:                     0.00011546000
ElSet #:                  167.00000000000
Rev @ Epoch:            42286.31052536559

STSORBIT PLUS Data Output to STSPLUS.LOG, Data = 17 
Satellite Name:         MIR Space Station
Catalog Number:         16609  86 17  A
Epoch Date/Time:        93192.12233796297
                        07/11/1993  02:56:10.000 UTC
ECI X:               -8617248.92526347200 ft
    Y:              -15077459.08108566000 ft
    Z:               13806887.09734187000 ft
    Xdot:               12614.26230523560 ft/sec
    Ydot:              -18214.71804776612 ft/sec
    Zdot:              -12006.04438377176 ft/sec
Ndot/2 (Drag):              0.00008567000
Nndot/6:                    0.00000000000
B-Star:                     0.00011546000
ElSet #:                  167.00000000000
Rev @ Epoch:            42286.35385448637

STSORBIT PLUS Data Output to STSPLUS.LOG, Data = 27 
Satellite Name:         MIR Space Station
Catalog Number:         16609  86 17  A
Epoch Date/Time:        93192.12280092592
                        07/11/1993  02:56:50.000 UTC
ECI X:                  -1333.74601094830 nm
    Y:                  -2598.74977950943 nm
    Z:                   2190.96899536823 nm
    Xdot:                   2.14691236531 nm/sec
    Ydot:                  -2.86693936350 nm/sec
    Zdot:                  -2.09121400862 nm/sec
Ndot/2 (Drag):              0.00008567000
Nndot/6:                    0.00000000000
B-Star:                     0.00011546000
ElSet #:                  167.00000000000
Rev @ Epoch:            42286.36107600650

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 88


NOTES:

1.   The X-Y-Z Cartesian State Vector is given as a standard Earth-centered 
     inertial ("ECI") cartesian 6-dimensional state vector where the X-Axis 
     is pointing toward the vernal equinox, the Z-Axis is pointing toward 
     the North Pole, and the Y-Axis is mutually orthogonal to the other 
     axes in a right-handed axis system. All coordinates are for true 
     equator and equinox of date.

2.   The units of measure for the state vector may be determined by the 
     tens digit of the Data Mode in the initial header line as well as 
     being indicated with the data:

      4   Kilometers and kilometers per second
     14   Feet and feet per second
     24   Nautical miles and nautical miles per second

3.   One data item is given per line, labeled as shown in the examples. The 
     data in the first four lines (Satellite Name, Catalog Number, and two 
     lines of Date/Time) begin in column 25. The remaining numeric data 
     items begin in column 21 and use a FORTRAN-like format statement 
     F21.11.

4.   The Catalog Number is given first as the NORAD Number ("16609" in the 
     example) and then as the IAU Designation ("86 17  A"). The IAU 
     Designation is separated from the NORAD Number by two spaces. Some 2-
     line elements omit the IAU Designation, in which case that portion 
     will be blank.

5.   Note that the Date/Time is presented on two lines in two different 
     formats. The first format is the NASA Day-of-Year ("DOY") format, 
     YYDDD.DDDDDD, since that is the format used by NASA/JSC for X-Y-Z 
     state vectors for the Space Shuttle, in 2-line elements, and in 
     program VEC2TLE. In the DOY format, time is counted from midnight 
     (00:00 UTC) each day. Some calculations may require instead the Julian 
     Date format which counts time from noon (12:00 UTC) each day. The 
     Date/Time is also "decoded" and given in the more conventional 
     "MM/DD/YYYY  HH/MM/SS.SSS" format for clarity using Coordinated 
     Universal Time (UTC/GMT).

6.   The ElSet Number is specified in the 2-line elements used to generate 
     the ground track and is always given as an integer. Note that ElSet 
     Numbers may not necessarily follow in sequence and that different 
     sources will use different sequences of ElSet numbers.

7.   The Rev Number at Epoch (the orbit number at the time the data is 
     sampled) is based upon the Rev Number specified in the 2-line elements 
     used to generate the ground track. The fractional part is calculated 
     by STSPLUS geometrically from the ascending node. Note that US Space 
     Command uses a different orbit numbering convention than does NASA for 
     space shuttle missions; US Space Command usually specifies the first 
     (partial) orbit number as Rev 0, while NASA specifies that orbit 
     number as Rev 1. For satellites which have been in orbit for long 
     periods of time, the Rev Number may be arbitrary.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 89


Data Mode 9: Pass Predictions
-----------------------------

   --------#20580 AOS--------  --MAX VISIBILITY--  ------LOS------
 #   UTC Date UTC Time    Azm  UTC Time Alt   Azm  UTC Time    Azm Duration
 1 02/27/1993 03:58:09  205.1  04:03:00   9 157.9  04:07:52  110.8  0:09:43
-+ ---------+---------  --+--  ----+---  -+ --+--  ----+---  --+-- ----+---
 |          |             |        |      |   |        |       |       |
 Pass #     |             |        |      |   |        |       |       |
            |             |        |      |   |        |       |       |
 +----------+             |        |      |   |        |       |       |
 |                        |        |      |   |        |       |       |
 |  +---------------------+        |      |   |        |       |       |
 |  |                              |      |   |        |       |       |
 |  +----- AOS Azimuth (degrees)   |      |   |        |       |       |
 |                                 |      |   |        |       |       |
 +-------- AOS Date/Time           |      |   |        |       |       |
           (mm/dd/yyyy hh:mm:ss)   |      |   |        |       |       |
                                   |      |   |        |       |       |
 +---------------------------------+      |   |        |       |       |
 |                                        |   |        |       |       |
 |  +-------------------------------------+   |        |       |       |
 |  |                                         |        |       |       |
 |  |  +--------------------------------------+        |       |       |
 |  |  |                                               |       |       |
 |  |  +-- MAX Azimuth (degrees)                       |       |       |
 |  |                                                  |       |       |
 |  +----- MAX Altitude (degrees)                      |       |       |
 |                                                     |       |       |
 +-------- MAX Time (hh:mm:ss)                         |       |       |
                                                       |       |       |
 +-----------------------------------------------------+       |       |
 |                                                             |       |
 |  +----------------------------------------------------------+       |
 |  |                                                                  |
 |  +----- LOS Azimuth (degrees)                                       |
 |                                                                     |
 +-------- LOS Time (hh:mm:ss)                                         |
                                                                       |
                                     Total Pass Duration (hh:mm:ss)  --+

NOTES:

1.   When the Data Output mode is set up for pass predictions, dates and 
     times for pass predictions may be selected for UTC/GMT or local time 
     and the selected time zone abbreviation and time scale will be used. 
     Substitute the appropriate abbreviation for "UTC" as required if other 
     than UTC has been selected. When UTC or GMT is selected, the Data Mode 
     will be given as "9"; when local time is selected, the Data Mode will 
     be given as "19".

2.   The Pass # is an arbitrary number assigned by STSPLUS during the pass 
     calculations and is a function of the real or simulated time at which 
     the calculations are performed. If the real or simulated time is 
     changed, the pass numbers may change and different passes may be 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 90


     shown.

3.   The satellite NORAD number is included in the heading, "20580" in the 
     sample above.

4.   The Date (UTC/GMT or local) is given only for AOS. Since a pass may 
     span 00:00:00 hours, the date for MAX VISIBILITY and/or LOS may have 
     to be incremented from that shown for AOS.

5.   All azimuths ("Azm") have been rounded to the nearest 0.1 degree; the 
     MAX VISIBILITY altitude ("Alt") has been rounded to the nearest 
     degree.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 91


F4     Calculate Satellite Positions with TRAKSTAR
--------------------------------------------------

     Tabular predictions for the currently selected satellite may be made 
by using TRAKSTAR by Dr. TS Kelso. STSPLUS has been arranged to operate 
seamlessly with TRAKSTAR by simply pressing Function Key F4 from the Main 
Menu. All data required by TRAKSTAR is automatically supplied by STSPLUS. 
See the section above "Predicting Satellite Passes with TRAKSTAR" and the 
TRAKSTAR documentation for full information.


F5     Set Launch Time and Date
-------------------------------

     Orbital data for the satellite must be loaded using the F2 command on 
the Main Menu before the launch date and time may be set or changed. Once 
saved in file STSPLUS.LTD, the launch date and time will be automatically 
read from that file each time the satellite is selected (see below).

                           ********************
                           *  IMPORTANT NOTE  *
                           ********************

     LAUNCH TIME AND DATE MUST EITHER BE INCLUDED IN FILE STSPLUS.LTD 
     OR BE MANUALLY ENTERED FOR EACH SATELLITE OR MISSION SINCE THAT 
     INFORMATION IS NOT INCLUDED IN 2-LINE ELEMENTS.

     Launch date and time are most important for manned missions such as 
the Space Shuttle since the mission timeline is reckoned using Mission 
Elapsed Time. However, MET may be used whenever actual launch date and time 
are known. The only requirement is that 2-line orbital elements must be 
available for the satellite. Since launch date and time are NOT included in 
the 2-line orbital elements, this means that you obtain the launch date and 
launch time independently and manually enter that data.
     Pressing F5 to enter launch date and time begins with the prompt:

     Enter Launch Time (HH:MM:SS):
       [Add 'U'or 'G' for UTC/GMT]

Enter the time in the format shown using 24-hour notation. Add the letter 
"U" to signify UTC (Coordinated Universal Time) or the letter "G" to 
signify GMT (Greenwich Mean Time, essentially identical to UTC for the 
purposes of this program). Use no suffix for local time; it will be 
internally converted to UTC/GMT. If you enter "U" or "G", the abbreviation 
used in the menus will be set to "UTC" or "GMT" respectively. One or two 
digit numbers may be used as required. [The comma is also acceptable as a 
separator in place of the colon.] You may omit seconds [or minutes and 
seconds] if desired. For example, an entry of "16" will be entered as 
16:00:00 or 4:00 PM. Press ENTER to leave the entry unchanged.

     Enter Launch Date (MM/DD/YYYY):
       [Enter '*' to clear LAUNCH DATE]

Enter the date in the format shown. Note that if you requested UTC or GMT 
when entering the time, the date is interpreted as the UTC/GMT date. The 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 92


full four digit year may be used OR two digits as in "92". Be sure to use 
the SLASH "/" rather than the MINUS "-" as the separator; STSPLUS's 
internal date algorithms will interpret the minus sign as just that and 
some rather strange dates can result! You may also use relative dates: -1 
will use the prior day, +2 will use two days hence, and so forth. Press 
ENTER to leave the date unchanged. Press "*" (followed by ENTER) to clear 
the launch date and time; this does NOT remove it from file STSPLUS.LTD.

     Press ENTER to accept, SPACE BAR to repeat:

When all data have been entered, the program pauses for your approval. If 
all data are correct, press ENTER. Press the SPACE BAR to start over. You 
are next asked if you wish to save this data:

     Add/Update this data in file STSPLUS.LTD [Y,n]:

Press "Y", "y" or ENTER to add or update the data in file STSPLUS.LTD (see 
below). Press "N" or "n" to use the data but not add or update it in file 
STSPLUS.LTD. Adding or updating the data to file STSPLUS.LTD makes sure 
that the launch date and time data will be available the next time this 
particular satellite is selected.


Using File STSPLUS.LTD for Launch Date & Time
---------------------------------------------

     An alternative and automatic method to set launch date and time is to 
use file STSPLUS.LTD. This file contains the NORAD number and launch date 
and time (UTC Julian date) for selected satellites. A sample entry appears 
as:

     22194,2448918.21503472,0
     --+-- -------+-------- +
       |          |         |
       |          |         +--- (Reserved, must be present)
       |          |
       |          +------------- Launch Date (UTC Julian date)
       |
       +------------------------ NORAD Number

The Sample above shows the data for Space Shuttle mission STS-52 (NORAD 
#22194) and corresponds to a launch date and time of 22 OCT 1992 @ 17:09:39 
UTC. The file is in standard ASCII format and may be edited with any 
standard editor; word processor users use the "non-document" mode. Use care 
when manually editing the file as STSPLUS performs NO ERROR CHECKING!
     Estimated 2-line orbital elements are usually available prior to a 
Space Shuttle launch, and actual 2-line orbital elements within about 8 to 
12 hours after a launch. Note, however, that the NORAD number is not 
assigned until actual launch and a "dummy" NORAD number is used for 
estimated pre-launch elements; for example, "00052" for STS-52. Once the 
launch has taken place, the permanent NORAD number is assigned. This change 
in NORAD number will require either that file STSPLUS.LTD be edited OR that 
a new entry be made. Note that there are still a few satellites around with 
low NORAD numbers!
     

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 93


     If file STSPLUS.LTD is present and if the selected satellite is found, 
the launch time and date will be set and Mission Elapsed Time (MET) will be 
used automatically; otherwise, T+Epoch (T+E) will be used. When MET is 
displayed, it may be changed to T+E by pressing F6 from the Main Menu 
(below) or F5 while the map is displayed.
     File STSPLUS.LTD is read each time a new satellite is selected using 
F2 from the Main Menu. If file STSPLUS.LTD is NOT present, the launch date 
and time will be saved in file STSPLUS.INI and must be MANUALLY MAINTAINED 
as in versions prior to 9245! If you wish to use the old method, rename or 
delete file STSPLUS.LTD.


F6     Set/Read/Save TDRS and Real Time Satellites
--------------------------------------------------

     STSPLUS is able to display up to 32 additional TDRS (or other 
geosynchronous/geostationary) or Real Time satellites. The first menu 
selection allows the user to select the desired satellite for each of the 
sixteen available "slots" as well as abbreviation, mode, and icon/label 
color. Note that these features are enabled and disabled using F10+F3+F2 
from the Main Menu. The following menu is displayed:

          TDRS and Real Time Satellite Maintenance Menu

          F1  Display/Modify satellite assignments
          F2  Save SCF Satellite Configuration File
          F3  Read SCF Satellite Configuration File
          F4  Clear Static and Real Time Satellites

          Press function key for desired menu or ENTER for Main Menu:

Press ENTER to return to the Main Menu, or press the desired function key 
to perform the indicated item.
     Before the current position of each satellite can be calculated, 2-
line elements must be read or updated using F2 from the Main Menu. After 
this has been performed once, the position will be calculated based upon 
those 2-line elements. The user is reminded that the 2-line elements should 
be updated periodically so that the calculated position accurately reflects 
the actual position.

NOTE:     Users of prior versions of STSPLUS will note that Function Key F6 
          has been reassigned for its present function. Switching between 
          MET and T+Epoch may now be accomplished ONLY by pressing F5 while 
          the ground track is displayed.

     F1  Display/Modify Satellite Assignments
     ----------------------------------------

     This menu selection displays the current TDRS and Real Time Satellite 
assignments and option selections as a table:


Program STSORBIT PLUS Satellite Orbit Simulation                   Page 94


--------------------------------------------------------------------------
         TDRS and Real Time Satellite Setup

Sat#  NORAD#   Abbr        Mode  Color Size  Label  Vis        Color Chart
   1   19883   TDRE      Static   10 o    3     ON
   2   21639   TDRW      Static   10 o    3     ON               1 = XXXXX
   3   22314   TDR5      Static    2 o    3     ON  OFF          2 = XXXXX
   4   19548   TDR2      Static    2 o    3     ON  OFF          3 = XXXXX
   5   13969   TDR1      Static    2 o    3     ON  OFF          4 = XXXXX
   6   16609   MIR    Real Time   12 o          ON   ON          5 = XXXXX
   7   21701   UARS   Real Time   13 o          ON  OFF          6 = XXXXX
   8   20580   HST    Real Time   14 o          ON  OFF          7 = XXXXX
   9   20638   ROSAT  Real Time   13 o          ON  OFF          8 = XXXXX
  10   22076   TOPEX  Real Time   13 o          ON  OFF          9 = XXXXX
  11       0         (not used)                                 10 = XXXXX
  12       0         (not used)                                 11 = XXXXX
  13       0         (not used)                                 12 = XXXXX
  14       0         (not used)                                 13 = XXXXX
  15       0         (not used)                                 14 = XXXXX
  16       0         (not used)                                 15 = XXXXX

Enter Satellite # to edit or press ENTER when done:
--------------------------------------------------------------------------

NOTE:     The first two satellite slots, #1 and #2, are reserved for the 
          standard TDRS East and TDRS West satellites, currently NORAD 
          Numbers 19833 and 21639. Instead of conventional circles of 
          visibility, these two satellites generate commumications coverage 
          circles. Assigning different satellites, especially satellites 
          which are not geostationary, may produce unpredictable results.

The Satellite Setup table headings indicate:

     Sat#      Satellite Assignment Number, 1 to 16.

     NORAD#    The NORAD Number of the assigned satellite, or "0" if no 
               satellite is assigned to this slot.

     Abbr      The five character abbreviation assigned to this satellite. 
               Use only letters and numbers; the common satellite name or 
               NORAD Number are the recommended choices. This abbreviation 
               will be used as a label on the map if the Label is ON.

     Mode      Three classifications are available: "Static" for 
               geosynchronous or geostationary satellites; "Real Time" for 
               satellites to be tracked dynamically; and, "(not used)" for 
               unassigned slots.

     Color     A number selected from the Color Chart at the right which 
               indicates the color to be used to display the satellite icon 
               and label (if enabled). Each "XXXXX" in the Color Chart 
               appears on color monitors as a bar of the corresponding 
               color. The "o" character to the right of the number is 
               displayed as a small diamond in the selected color.


Program STSORBIT PLUS Satellite Orbit Simulation                   Page 95


     Size      For Static satellites only, selects the relative size of the 
               icon used to represent the satellite. Values may range from 
               3 to 6. This column is blank for Real Time satellites since 
               the icon size is fixed for these satellites.

     Label     May be set to "ON" or "OFF" to indicate if the satellite 
               abbreviation is to be displayed. The label color will be the 
               same as that selected for the satellite.

     Vis       May be set to "ON" or "OFF" to indicate if the satellite 
               circle of visibility is to be drawn. The circle of 
               visibility is drawn only for Static satellite on normal maps 
               but is drawn for all satellites on Motion maps.

     Color     The color chart displays the 15 available icon and label 
     Chart     colors (BLACK is omitted). When a monochrone display is used 
               and the "/M" command line option is specified, two levels of 
               gray will normally be displayed instead of colors. Each 
               color is assigned a standard color number which is used for 
               all data entries.

     As indicated by the prompt, simply press ENTER if all data in the 
Satellite Setup is correct. You will return to the F6 menu above. If you 
wish to add a satellite or change the selections for an existing satellite, 
enter the satellite slot number (Sat# in the left column of the table). The 
following prompts will be displayed in turn:

          Enter NORAD Number:
          (Enter 0 to clear the satellite entry)

STSPLUS expects the NORAD number for the desired satellite. This number 
will be used to "capture" the 2-line elements when this satellite is 
subsequently displayed.

          Enter Satellite Abbreviation:

Enter any desired abbreviation, 5 characters or less, or the NORAD number. 
Use only letters, numbers, and the period ("."), dash ("-"), and comma 
(",") with no leading spaces.

          Enter Mode (0=STATIC, 1=REAL TIME):

Enter "0" or "1". STATIC mode satellites are drawn each time the map is 
redrawn on the screen. REAL TIME satellites are updated every 10 seconds or 
as often as the processor can complete the required calculations.

          Enter satellite color (1 to 15):

Enter the number for the desired color, as shown on the Color Chart at the 
right of the screen. An illegal color number will default to YELLOW.

          Display satellite Label (0=NO, 1=YES):

Enter "0" or "1". The label will be displayed directly below the satellite 
icon in the same color as that selected for the icon in the preceeding 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 96


step. For Real Time satellites, the label is only drawn when the map is 
redrawn and remains stationary EXCEPT when using the Motion Map (in which 
case it follows with the icon).

          Display Cir of Visibility (0=NO, 1=YES):

Enter "0" or "1". The circle of visibility is drawn (when enabled) for all 
Static satellites, and also for all Real Time satellites when using the 
Motion Map.
     When a new satellite is entered, a double asterisk ("**") will appear 
at the right for that satellite slot. This is to remind the user to display 
the ground track for that satellite so that 2-line elements may be stored 
in the TLE memory associated with that slot. The following message will 
also appear below the chart:

          **  Display ground track for this satellite!

To display the ground track, press F2 from the Main Menu, select the file 
of 2-line elements which includes the satellite in question, and enter the 
NORAD Number ("#nnnnn", where "nnnnn" is the NORAD Number). Once the 
satellite has been displayed on the map, the 2-line elements will be saved 
for future use.
     Although 2-line elements are saved for all TDRS and Real Time 
satellites, the user is reminded that these elements have a limited 
lifetime. That lifetime varies considerably from satellite to satellite. 
For geosynchronous satellites, 4 to 8 weeks is probably reasonable; for 
other active satellites, 1 to 2 weeks should be an upper limit before new 
elements are used. Use F2 from the Main Menu and enter the satellite name 
as "&" to scan through the 2-line elements file and update all elements 
which are more recent than those now saved.

F2  Save SCF Satellite Configuration File
-----------------------------------------

     Users may wish to switch among several sets of TDRS and Real Time 
satellites from time to time. Since it can be tedious to re-enter all the 
information repeatedly, STSPLUS can save and read Satellite Configuration 
Files, identified by the filetype .SCF. All parameters are saved and 
restored, exactly as if entered at the time. The current satellite 
configuration is automatically saved in file STSPLUS.INI each time the 
program is exited and is restored when the program is restarted. The 
following prompt is displayed:

          Save SCF Satellite Configuration File

          Enter FILENAME (without .SCF filetype), ENTER to quit:

Enter any desired filename WITHOUT the .SCF filetype; STSPLUS automatically 
appends the filetype and will reject any filename which includes a 
filetype. Filenames may be no longer than 8 characters.
     If the file already exists, STSPLUS will display a warning message:

          File STANDARD.SCF already exists! Overwrite [y/N]:

where "STANDARD.SCF" will be the requested file including the .SCF 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 97


filetype. Press "Y" or "y" to allow the existing file to be overwritten; 
press any other key to cancel the write operation, and then press ENTER to 
resume program operation. If the file does not exist, it will be created. 
Do not use filename STSPLUS since a sample file by that name is included 
with the distribution package (unless you wish to overwrite the supplied 
file).


F3  Read SCF Satellite Configuration File
-----------------------------------------

     See the comments above for saving SCF files. The following prompt is 
displayed:

          Read SCF Satellite Configuration File

          Enter FILENAME (without .SCF filetype), ENTER to quit:

          Available .SCF files are:

          STANDARD.SCF
          STSPLUS.SCF

STSPLUS displays a list of available SCF files, up to a maximum of 90 
files. Press ENTER to cancel the operation. Type the desired filename 
WITHOUT the .SCF filetype; STSPLUS automatically appends the filetype and 
will reject any filename which includes a filetype. Filenames may be no 
longer than 8 characters. If the file does not exist, an error message will 
be displayed.


F4  Clear Static and Real Time Satellites
-----------------------------------------

     Use this function to clear all static and real time satellites, 
numbers 3 through 32. STSPLUS asks the user to confirm the operation to 
avoid accidental clearing. 
     NOTE: Slots 1 and 2 are reserved for TDRS satellites and should ALWAYS 
contain TDRS or similar geosynchronous satellites. The program may perform 
unpredictably if these slots are cleared or have other types of satellites.


F7     Set FILENAMES and PATHS
------------------------------

     Function Key F7 allows the user to select the paths and/or filenames 
for the various files that STSPLUS uses to select satellites, tracking 
stations, and other features:

          Select path or filename to set, press ENTER when done:

            F1  Set 2-LINE ELEMENTS path:      [I:\TLE\]
            F2  Set TRACKING STATION filename: [STSPLUS.TRK]
            F3  Set MAP DATABASE FILES path:   [D:\MAPDATA\]
            F4  Set FEATURES LABEL filename:   [STSPLUS.LOC]

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 98


            F5  Set TRAKSTAR path:             [D:\STSPLUS\]
            F6  Set CITYFILE filename:         [STSPLUS.CTY]

          Enter selection or ENTER:

Press the indicated function key for the item you wish to change. The 
current path or filename is shown in square brackets for each selection. 
Press ENTER to leave a path or filename unchanged. The following is a 
typical prompt for filename:

          Enter TRACKING STATION filename: _
          (Press ENTER to leave unchanged)

     For filenames, enter the full filename including filetype. A drive and 
directory may also be included if desired. If no filetype is entered, 
STSPLUS will automatically supply ".TRK" for tracking station files, and 
".LOC" for features label files. If the desired file has no filetype, 
include the period in the filename entered (e.g. "STATION.") to prevent the 
automatic addition of a filetype.
     For the path selections, enter the desired drive and subdirectory. The 
trailing backslash will automatically be added if it is omitted. If the 
path cannot be found, an error message will be displayed and the path will 
default to the current drive and directory. For best performance, use a RAM 
disk for Map Database Files; see the section "Using a RAM Disk" for further 
information.
     After each entry, the Path and Filenames Menu is again displayed with 
the current selections. Press ENTER when done to return to the STSPLUS Main 
Menu.


F8     Set Program TIME and DATE
--------------------------------

     This menu provides a number of time and date functions for use 
with STSPLUS. The program clock may be set to real or simulated time 
using several methods, current clock corrections applied by program 
RIGHTIME may be displayed, and the UTC OFFSET and DAYLIGHT Flag may be 
adjusted.
     It is often convenient to set the TIME and DATE within STSPLUS to 
something other than the current system time and date, or to return to the 
current system time and date if the program time and date have been 
changed. Press F8 to go to the TIME and DATE Menu:


                              Program STSORBIT PLUS

                  Space Shuttle and Satellite Orbit Simulation
                                  Version 9338

                   Current time:  14:52:24 PST   22:52:24 UTC
                   Current date:    03/10/1993     03/10/1993

                    ACTUAL SYSTEM DATE AND TIME SHOWN ABOVE
                             (Assisted by RIGHTIME)


Program STSORBIT PLUS Satellite Orbit Simulation                   Page 99


         F1     Restore SYSTEM date and time (use "real time")
         F2     Set DOS SYSTEM CLOCK using calendar date and time
         F3     Set SIMULATED date and time using calendar date and time
         F4     Set SIMULATED date and time using Mission Elapsed Time

         F9     Display Current RIGHTIME Corrections
         F10    Set UTC OFFSET and DAYLIGHT Flag

         ENTER  Return to MAIN MENU

         Select desired function:


     The Date and Time Menu, shown above, displays the available time 
setting functions along with the actual system date and time as determined 
by the DOS software clock in your computer (even if simulated time is in 
effect). If program RIGHTIME Version 2.5+ is currently enabled, the message 
"(Assisted by RIGHTIME)" will also appear. Both your local date and time, 
"PDT" or Pacific Daylight Time in the example, and "UTC" (Coordinated 
Universal Time) date and time are displayed. If times have been set using 
the letter "G", the abbreviation at the right will be "GMT" (Greenwich Mean 
Time).
     Press ENTER to return to the Main Menu with the date and time as 
displayed on the screen (Current or Simulated).
     If you wish to execute STSPLUS in "real time", cancelling any 
simulated time that may be in effect, use the F1 command. This will restore 
the time and date used for the tracking display to that shown at the top of 
the menu. If the actual system date or time displayed is incorrect, use 
program TIMESET (if available) or the F2 command to correctly set your 
system clock.
     Some organizations, NASA for example, continue to use the wording 
"Greenwich Mean Time" or "GMT" for what is now usually referred to as 
"Coordinated Universal Time" or "UTC" (and sometimes, depending upon the 
application, as "UT", "UT1" or "UT2"). STSPLUS uses Coordinated Universal 
Time or "UTC", the time used for civil timekeeping and broadcast by radio 
stations such as WWV and the BBC. Although technically these different time 
standards are not exactly the same, the difference is only a maximum of 0.9 
seconds and the program treats them all as identical. STSPLUS defaults to 
the abbreviation "UTC" but if you prefer to use "GMT", enter any simulated 
time using F3 and include the letter "G" (upper or lower case) at the end. 
The time abbreviation at the top of the screen will change from "UTC" to 
"GMT" and will continue using that abbreviation until a time is entered 
suffixed with "U". 
     Times are always entered as "HH:MM:SS" where HH is HOURS, MM is 
MINUTES, and SS is SECONDS. The time entry format is very flexible. Leading 
zeroes are not required. The comma (",") may be used in place of the colon 
(":") as a separator if desired. SECONDS or MINUTES and SECONDS may be 
omitted if desired. Time entries are assumed to be local time; to enter UTC 
or GMT times, add the letter "U" or "G" (upper or lower case) respectively 
following the entry. For example, the following are valid time entries:

          Entry          Interpreted as
          ------         --------------------------
          12             12:00:00 (LOCAL TIME ZONE)
          13,1           13:01:00 (LOCAL TIME ZONE)

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 100


          4:1:15         04:01:15 (LOCAL TIME ZONE)
          1,1,1          01:01:01 (LOCAL TIME ZONE)
          13,45U         13:45:00 UTC 
          1:20g          01:20:00 GMT

     Dates are entered as "MM/DD/YYYY" or "MM/DD/YY" where MM is MONTHS (as 
a number from 1 to 12), DD is DAYS, and YYYY is the full four-digit YEAR or 
YY is the last two digits of the YEAR. Except for the two digit year 
option, the full date must always be entered; leading zeroes are not 
required. The date entered is assumed to be for the same time zone as the 
time entered. If local time is entered, the date will be treated as the 
local date; if UTC (or GMT) time is entered, the date will be treated as 
the UTC/GMT date.
     After a time or date entry has been accepted (after you press the 
ENTER key), STSPLUS reformats the entry to its standard format, clears the 
characters you entered, and replaces them by the standard format in both 
local and UTC/GMT time zones. This provides a double check that the program 
has interpreted your entry as you wished.

F1     Restore System Date and Time
-----------------------------------

     Press F1 to restore the program date and time to the system date and 
time. This command reads the DOS clock and restores the program to "real 
time" operation. If the program date and time have not been changed with 
the F3 or F4 commands, this command will have no effect.

F2     Set DOS System Clock
---------------------------

     Press F2 to set the DOS system clock. Use this command if you wish to 
change the actual date and time on your system. Note that on many systems 
using DOS 3.3 or higher, this command will set BOTH the software clock AND 
the hardware clock.

                               *************
                               *  CAUTION  *
                               *************

     This function should NOT be used when program RIGHTIME is 
     regulating the DOS clocks UNLESS no other method is available. 
     Use program TIMESET to set the DOS clocks accurately instead!

                              Program STSORBIT PLUS

                  Space Shuttle and Satellite Orbit Simulation
                                  Version 9338

                   Current time:  19:59:10 PST   03:59:10 UTC
                   Current date:    02/24/1993     02/25/1993

        CAUTION: This function will change the computer's SYSTEM CLOCK!

                     Press ENTER to leave an item unchanged


Program STSORBIT PLUS Satellite Orbit Simulation                   Page 101


              Enter TIME (HH:MM:SS):                16:34:24 PST
              Enter DATE (MM/DD/YYYY):                 4/08/1992

         Press ENTER to accept, SPACE BAR to repeat: _

The sample above shows the screen after the time and date entries have been 
completed. The current ACTUAL system date and time are displayed for 
approval. Press ENTER to accept the time and date displayed, or press the 
SPACE BAR to repeat the entries.

F3     Set Simulated Date and Time using Calendar Method
--------------------------------------------------------

     Press F3 to set a simulated date and time. The date and time may be 
either in the past or in the future. This command does NOT affect the DOS 
clock in your system! Use the F1 command above to restore the date and time 
to "real time".

                              Program STSORBIT PLUS

                  Space Shuttle and Satellite Orbit Simulation
                                  Version 9338

                   Current time:  19:59:10 PST   03:59:10 UTC
                   Current date:    02/24/1993     02/25/1993



                     Press ENTER to leave an item unchanged

         Enter SIMULATED TIME  [12:05:06]:     13:00:00 PST   21:00:00 UTC
         Enter SIMULATED DATE  [11/11/1991]:     11/09/1991     11/09/1991

         Press ENTER to accept, SPACE BAR to repeat: _

The sample above shows the screen after the time and date entries have been 
completed. The new SIMULATED date and time are displayed (and counting) for 
approval. Press ENTER to accept the time and date displayed, or press the 
SPACE BAR to repeat the entries.

F4     Set Simulated Date and Time using MET
--------------------------------------------

     Press F4 to set a simulated date and time using MET (Mission Elapsed 
Time). Note that this command will appear ONLY if the mission name begins 
with the letters "STS", signifying a Space Transportation System (Space 
Shuttle) mission AND if a launch time and date have previously been 
entered.

                              Program STSORBIT PLUS

                  Space Shuttle and Satellite Orbit Simulation
                                  Version 9338

                  Simulated time:  00:17:18 PST   08:17:18 UTC

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 102


                  Simulated date:    10/09/1992     10/09/1992



                    Enter desired Mission Elapsed Time (MET)

                    Enter MET DAY (NN):             3 day(s)
                    Enter MET TIME (HH:MM:SS):      04:30:00 MET

                    Press ENTER to accept, SPACE BAR to repeat: _

The sample above shows the screen after the day and time entries have been 
completed. The Mission Elapsed Time is immediately converted to actual date 
and time and the current SIMULATED date and time, based upon the MET just 
entered, are then displayed (and counting) for approval. Press ENTER to 
accept the time and date displayed, or press the SPACE BAR to repeat the 
entries.

F9     Display Current RIGHTIME Corrections
-------------------------------------------

     If program RIGHTIME has been detected, the "F9" menu item will be 
displayed and you may press F9 to display the time since the last TIMESET, 
the current WARM correction, and the current COOL correction:

                        RighTime Version 2.53 detected!


                   Time Since Last TIMESET:   0 days 08:58:20

                   Current WARM Correction:   -0.01 seconds
                   Current COOL Correction:   -0.35 seconds

                   Press any key to continue ... _

The version of RIGHTIME is displayed. The time since the last TIMESET is 
saved by program RIGHTIME to the nearest 200 seconds and will therefore not 
change until that increment is reached. The time is shown as days followed 
by hours:minutes:seconds. If more than 7 days has elapsed since the last 
TIMESET, an additional message "(TIMESET suggested!)" will also appear. The 
WARM and COOL corrections are shown and are updated when the system time is 
set using Function Key F1 from this menu, by program TIMESET, or by other 
means. Press any key, such as ENTER, to return to the Time and Date Menu.

F10    Set UTC OFFSET and DAYLIGHT Flag
---------------------------------------

     You may change the UTC Offset and/or the setting of the Daylight Flag 
using F10. The prompts are self-explanatory; see the section "Program 
Options and Features, Set UTC Offset and Daylight Flag" for a detailed 
description of the UTC Offset and Daylight flag.



Program STSORBIT PLUS Satellite Orbit Simulation                   Page 103


F9     DOS Shell (CAUTION: DOS Version 3.x+ ONLY!)
--------------------------------------------------

     If a system function is desired at the Main Menu, press F9 to execute 
BASIC's DOS SHELL function. This will return you to a DOS prompt and most 
DOS commands may be executed immediately. When the Shell is executed, 
STSPLUS remains in memory and the map data will not be re-read when you 
return. All files used by STSPLUS are closed. However, this means that a 
substantial amount of memory is in use and not available to DOS during the 
shell operations. Enter "EXIT" (without the quotation marks and followed by 
ENTER) at the DOS prompt when you wish to return to STSORBIT. 

     CAUTION: The BASIC SHELL function is only reliable for versions of DOS 
     of 3.0 or higher! Systems with less than 640K memory may fail to 
     execute the shell and applications requiring large amounts of memory 
     may also fail.

F10    Set STSORBIT PLUS Program Options and Features
-----------------------------------------------------

     A number of program features and display options are set using the F10 
Program Options Menu. These selections are further described in the section 
"Program Options Menu" below.

ENTER  Resume Mission
---------------------

     Pressing ENTER resumes the current mission shown in parentheses to the 
right of the command on the Main Menu. The 2-line elements file from which 
the data was read is shown in square brackets.

         ENTER  Resume Mission                  (STS-41 [STS41F])

Any manually entered data is retained. "ENTER" means the key marked ENTER, 
RETURN, or with a left pointing arrow -- but not the backspace or cursor 
position keys which may also be marked with arrows! (I am afflicted with 
too long a memory; once upon a time this function was known as Carriage 
Return and was often shortened to RETURN or even CR. With the advent of 
electronic typewriters, video terminals, dot matrix printers and all the 
rest, "carriages" have long since disappeared but old habits die hard! Most 
PC keyboards are now marked with "ENTER".)
     Use ENTER to resume plotting a mission in progress after returning to 
the Main Menu to perform some change (such as enabling the node display, 
enabling the NASA tracking stations, or adjusting the time or date).


ESC    Quit STSORBIT PLUS and Save Current Mission
--------------------------------------------------

     Press ESC (the key marked "ESC" or "Esc", not the letters E+S+C) to 
quit program STSORBIT PLUS. If you press ESC to quit the program and have 
manually entered orbital data, STSPLUS will save all required mission data 
in file STSPLUS.INI prior to terminating. This will be the data available 
with the ENTER key the next time you execute the program. The demonstration 
data will not be saved, preserving any previously saved mission data.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 104


     When you have finished with STSPLUS, press ESC at the Main Menu to 
return to DOS. The data (and any adjustments you have made) for the current 
mission are saved in file STSPLUS.INI, but the map data is lost and will be 
re-read when you next use program STSPLUS.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 105


PROGRAM OPTIONS AND FEATURES MENU
---------------------------------

     A number of program features and display options are set using the F10 
Program Options Menu. When used with CGA displays, the features shown below 
as selected by function keys F3 and F4 are not available because of the low 
resolution of the CGA display. The following Options Menu is displayed when 
the F10 command is entered from the Main Menu:


                              Program STSORBIT PLUS

                  Space Shuttle and Satellite Orbit Simulation
                                  Version 9338

                   Current time:  19:59:10 PST   03:59:10 UTC
                   Current date:    02/24/1993     02/25/1993


         F1             Program STSORBIT PLUS Information
         F2             Set New Local Coordinates (Rancho Palos Verdes, CA)
         F3             Select Display Features
         F4     A/A     Select Satellite Coordinates: RA/DEC, Alt/Az or XYZ
         F5     OFF     Show Ascending & Descending Node Data
         F6     ORTHO   Set Map Projection and Size
         F7     OFF     Enable/Disable EVENT TIMERS
         F8     ON      Enable/Disable Audible ALARMS
         F9    -7.00    Set UTC Time Offset and Daylight Flag
         F10    OFF     Enable/Disable Printer Logging

         ENTER          Return to MAIN MENU

         Select desired function:


F1     Program STSORBIT PLUS Information
----------------------------------------

     Function Key F1 displays information about program STSORBIT PLUS 
including the copyright notice, version number, my name and address, and 
the telephone number of my RPV ASTRONOMY BBS (Bulletin Board System). The 
current version of STSORBIT PLUS is always posted on the BBS. The BBS has a 
power controller; if it hasn't answered after the THIRD RING, hang up and 
call back in two minutes. The BBS is available 24 hours per day at 9600, 
2400 and 1200 baud.


F2     Set New Local Coordinates
--------------------------------

     In order to perform the calculations related to satellite visibility 
and altitude/azimuth, STSPLUS must know the geographic coordinates for the 
user's location. The name of the current location is shown in parentheses. 
When STSPLUS is first started, the default coordinates are set to Rancho 
Palos Verdes, California, near Los Angeles. The current location is 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 106


indicated by the name in parentheses on the Options Menu. The program 
provides two methods for setting your own coordinates: reading a file of 
city names and coordinates (STSPLUS.CTY); or manually entering the 
information.
     Pressing F2 will display the following reminder:

     STSPLUS searchs STSPLUS.CTY for the CITYNAME you enter anywhere in the
     city names. 'SAN' appears in 'SAN DIEGO', 'SANTA ANA', 'THOUSAND OAKS.

     Press ENTER to delete SECOND LOCATION, or enter '*' to manually enter
     a city name and coordinates (and optionally add it to STSPLUS.CTY).

     In other words, when you enter a name or partial name, STSPLUS will 
attempt to match that group of characters anywhere in the names which 
appear in the city file. For example, 'SAN' matches 'SAN diego' as well as 
'SAN jose' and 'thouSANd oaks'. To get 'SAN FRANCISCO' on the first try, 
enter 'SAN F' with a space between the 'N' and 'F'. Case is not 
significant; upper and lower case letters are treated identically. If you 
change your mind and wish to cancel the operation, simply press ENTER by 
itself. Use BACKSPACE to make corrections.
     To begin the search, enter the desired name after the prompt. In the 
example which follows, the name 'ran' was entered for the search.

     Enter CITYNAME to match:    ran

     Processing record  1
       City Name:  Rancho Palos Verdes CA
       Latitude:     33.7675
       Longitude:  -118.4033
       Elevation:   186 meters

     Press ENTER to ACCEPT this city as your location, OR
     Press TAB to also display this city's location, OR
     Press SPACE to search for next city:  _

     If the city displayed is the one you wish to use as your local 
coordinates, press ENTER. If you wish to display this city as a second 
location on the display, press TAB. The data will be entered into STSPLUS 
and subsequently saved in file STSPLUS.INI. If you wish to search further 
in the file, press the SPACE BAR.

     NOTE: The elevations contained in file STSPLUS.CTY are almost all zero 
     except for Rancho Palos Verdes, CA for which I have accurate elevation 
     above mean sea level. If you know the correct elevation for your 
     location, edit the file using any ASCII text editor and change the 
     last number on the line. STSPLUS.CTY contains over 800 cities. If 
     users send me their correct elevations (or additional cities they wish 
     added), I will incorporate that data into subsequent versions of file 
     STSPLUS.CTY.

     To enter location data manually, press "*" (without the quotation 
marks) followed by ENTER. You will be prompted for the city name, latitude, 
longitude, and elevation. Latitude and longitude may be entered using three 
different formats for convenience (note the use of comma and decimal 
point):

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 107



          DDD.DDDDD           Degrees and decimal fraction
          DD,MM.MMM           Degrees, minutes and decimal fraction
          DD,MM,SS.SS         Degrees, minutes, seconds and fraction

Note that SOUTH latitude and WEST longitude must be entered as NEGATIVE 
numbers as measured south of the Equator or west of the Prime Meridian at 
Greenwich, respectively. The default unit for elevations is meters above 
mean sea level; add "F" (upper or lower case without the quotation marks) 
if you wish to use feet.
     After the elevation has been entered, the data will be displayed for 
approval. All data are converted to degrees or meters as appropriate, 
regardless of the units used on input.

       City Name:  Rancho Palos Verdes CA
       Latitude:     33.7675
       Longitude:  -118.4033
       Elevation:   186 meters

     Press ENTER to ACCEPT this city, OR
     Press SPACE to cancel this data:  _

Press ENTER to accept the data as shown or SPACE to cancel the data and 
return to the Options Menu. If the data is accepted, STSPLUS will ask if 
you wish to append (add) this city/location to the existing file 
STSORBIT.CTY so that it will be automatically available thereafter.

     Do you with to append this data to file STSPLUS.CTY (Y/n):  _

Press "Y" or ENTER to append the data to the file, or press "N" to not 
modify the STSPLUS.CTY file.


F3     Set Display Features
---------------------------

     A number of display features may be enabled or disabled using a 
separate sub-menu. See the section SET DISPLAY FEATURES below for a full 
description.


F4     Select Satellite Coordinates
-----------------------------------

     The F4 command may be used to select the units used to display the 
current coordinates for the satellite. The choices are:

     RA/DEC    Right Ascension and Declination (Equator and Equinox of 
               Date).

     Alt/Az    Altitude and Azimuth. Altitude is the elevation above the 
               horizon (assuming mean sea level), and azimuth is the 
               direction in the sense NESW (North to East to South to 
               West).


Program STSORBIT PLUS Satellite Orbit Simulation                   Page 108


     XYZ       Geocentric Cartesion Coordinates. The X-Axis and Y-Axis are 
               aligned with the Equator with the X-Axis pointing in the 
               direction of the Vernal Equinox. The Z-Axis points toward 
               the North Pole.


F5     Show Ascending & Descending Node Data
--------------------------------------------

     The nodes of an Earth orbit are the points on the ground track where 
the path crosses the Equator. The ascending node crosses from South to 
North and the descending node crosses from North to South. Orbit numbers 
normally increment at the ascending node. This command adds two additional 
lines of data at the lower left of the screen giving the time (MET or time 
since epoch) and longitude of the most recent ascending and descending 
nodes. This information is useful when comparing STSPLUS's data against 
other sources such as the wall map in Mission Control.


F6     Set Map Projection and Size
----------------------------------

     The F6 command selects the size and field of view of the displayed 
map. By default, the map is displayed using the orthographic projection, 
"ORTHO", shows one complete hemisphere, and is centered so that the 
selected satellite is visible. This corresponds to a magnification factor 
of 100%.
     Pressing F6 will select between WORLD, QUAD, ZOOM, and ORTHO maps. 
Selecting WORLD will display the full world using rectangular projection 
centered on the Prime Meridian at Greenwich, England at 0 degrees 
longitude or at the International Date Line at 180 degrees longitude. 
Selecting QUAD will select one of twelve Quadrant Maps showing a field of 
view (horizontal size) of 180 degrees using rectangular projection. 
Selecting ZOOM will select a Zoom Map with field of view adjustable from 30 
degrees to 180 degrees; the default field of view is 75 degrees; the Zoom 
Map is approximately centered on the current ground track position of the 
satellite. Selecting ORTHO will select the orthographic projection. See the 
sections ORTHOGRAPHIC MAPS, QUADRANT MAPS, ZOOM MAPS, and AUTOMATIC MAP 
GENERATION for additional information.


F7     Enable/Disable EVENT TIMERS
----------------------------------

     Press F7 to enable or disable all event timers. Event timers are 
enabled by default if file STSPLUS.INI is present. Especially while the map 
is being drawn, the calculations associated with the event times require 
appreciable time. If the event timers are disabled, the audible alarms will 
also be disabled. See the section "Event Timers and Audible Alarms" for a 
full discussion of the event timers.



Program STSORBIT PLUS Satellite Orbit Simulation                   Page 109


F8     Enable/Disable Audible ALARMS
------------------------------------

     Provided event timers are enabled (above), you may press F8 to enable 
or disable audible alarms. Many users allow their computer to run STSPLUS 
while performing other tasks and the audible alarm will alert them to an 
imminent AOS (Acquisition of Signal) or LOS (Loss of Signal) event 
associated with either their local circle of visibility or the TDRS 
communications satellites.
     For the local circle of visibility, an "up/down" tone sounds six times 
two minutes prior to AOS and five tones sound thirty seconds prior to LOS. 
Provided TDRS coverage is enabled (F10+F3+F2 from the Main Menu), three 
brief tones sound thirty seconds prior to AOS or LOS. Provided Sun features 
are enabled (F10+F3+F8), two tones will sound approximately thirty seconds 
before orbital sunrise and sunset. The characteristics of the audible tones 
will thus allow the user to identify what kind of AOS or LOS event is about 
to happen.
     Depending upon the computer and the version of DOS being used, "music" 
such as these audible alarms may cause the DOS clock to lose a small amount 
of time each time an alarm sounds. The amount of time loss is quite small 
but may accumulate over long periods of time. (The DOS clock may also run 
either fast or slow and effectively mask the time loss due to sound 
effects.)


F9     Set UTC Time Offset and Daylight Flag
--------------------------------------------

     STSPLUS uses UTC or Coordinated Universal Time, an adjusted version 
of Universal Time (which STSPLUS considers the same as GMT or Greenwich 
Mean Time), for certain functions such as launch time. The difference 
between UT, UT1, UT2 and UTC is never more than 0.9 seconds. UTC is used 
because it is the standard for civil timekeeping and agrees with standard 
atomic time, TDB or Terrestrial Barycentric Time, used by astronomers. 
However, NASA continues to use the GMT designation, a holdover from earlier 
days before the introduction of UTC. Using UTC permits critical data to be 
used across many time zones without conversion. However, it also means that 
STSORBIT must know what number of hours to add to UTC in order to obtain 
your local time, and whether or not you are currently using daylight 
savings time (summer time in the UK).
     When prompted, enter the time offset in hours from your local time to 
Coordinated Universal Time. Examples are shown for most time zones in North 
America. STSPLUS then asks if you are using daylight savings time; enter 
"0" if not, and "1" if so. The sum of these two values is shown on the Main 
Menu; for example, if the computer is set to Pacific Daylight Time (UTC 
offset is -8.00 hours and Daylight Flag = 1), the sum will be -7.00. For 
most time zones in North America, the correct zone abbreviation will be 
shown on the ground track display for Local date and time. When you change 
your computer from/to daylight savings time, use this command to update 
STSPLUS. The following shows the display when using the F9 command:


Set UTC TIME ZONE OFFSET and DAYLIGHT FLAG

     STSPLUS must know the difference between your local time zone and 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 110


Coordinated Universal Time (UTC), also sometimes known as Greenwich Mean 
Time (GMT). With this information, STSPLUS can automatically adjust launch 
or Epoch times and dates for your local time zone. In addition, STSPLUS 
must know if your computer is now set to STANDARD or DAYLIGHT time.
     First, enter the difference between your STANDARD time zone and UTC in 
hours. Do NOT include the hour for daylight time if you are now on DAYLIGHT 
time; it will be entered separately. For most time zones in the United 
States and Canada, the entries required are:

          Eastern Standard Time     EST    -5.0
          Central Standard Time     CST    -6.0
          Mountain Standard Time    MST    -7.0
          Pacific Standard Time     PST    -8.0

          Enter UTC Offset (hours):          -8
          Enter DAYLIGHT Flag (0=OFF, 1=ON): 1


Once this information has been entered, it will be saved in file 
STSPLUS.INI and will not be requested again. If you change from Standard to 
Daylight Time or vice versa, use the F10+F9 command to update the Daylight 
Flag.
     If you change the setting of the Daylight Flag, STSPLUS will ask if 
you wish to adjust your DOS software clock:

          You have changed the setting of the Daylight Flag.

          Do you wish to adjust your DOS clock to reflect the
          change [y/N]:

If you have already made the change at the DOS prompt (or using some other 
software) or do not wish to change the DOS clock, press ENTER (or type "N" 
followed by ENTER). If you wish to adjust the DOS clock to correspond to 
the new setting of the Daylight Flag, press "Y" followed by ENTER. When 
STSPLUS changes the DOS clock, it synchronizes the time change to the 
nearest second but there may be a small error introduced; only if your 
computer is precisely set would the error be detectable.

                               *************
                               *  CAUTION  *
                               *************

For computers equipped with 80286 or higher processors AND using DOS 3.2 or 
higher, changing the DOS clock will ALSO change the hardware clock. 8088-
based computers may or may not have a hardware clock installed and, even if 
a hardware clock is present, it may or may not be compatible with the DOS 
time setting commands.


F10    Enable/Disable Printer Logging
-------------------------------------
     I have found it interesting to log the orbital data and the ascending 
and descending node information on my printer when analyzing the mission 
data over long periods of time. The F10 command toggles the printer logging 
function on and off. The first page of the log includes the current orbital 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 111


data and subsequent pages contain only node information. In addition to the 
information presented on the display, the printer log also calculates the 
current orbital time, the time from one ascending (descending) node to the 
next, for the third and subsequent nodes. A typical log is shown below. 

     IMPORTANT:     BE SURE THE PRINTER IS TURNED ON PRIOR TO ENTERING THE 
                    F10 COMMAND. 

STSORBIT: Space Shuttle Tracking Program, Version 9338          Page 1

ORBITAL DATA for STS-31 Discovery/HST

          NORAD Number:            20580
          Launch Date:             04/24/1990
          Launch Time:             05:33:52
          Orbit Inclination:       28.4695
          Orbit Altitude:         329.50 nm

                UT DATE   UT TIME ORBIT    LONG           MET     TIME
Ascend Node: 04/28/1990  20:32:52    70  -69.95    4/14:58:07
Dscend Node: 04/28/1990  21:20:52    70   97.64    4/15:46:35
Ascend Node: 04/28/1990  22:09:52    71  -94.77    4/16:35:02  1:36:55


     When printer logging is enabled and the ground track is displayed, the 
word "LOG" will appear in red at the right of the text area. Enabling 
printer logging also automatically enagles the display of ascending and 
descending node information.
     The Launch Date and Launch Time entries are given if that information 
has been entered indepentently. The Epoch Date and Epoch Time are always 
shown. Note also that the orbit altitude shown is the altitude at the time 
the log was started and will not be correct for subsequent entries, 
especially if the satellite has an elliptical orbit (high eccentricity).
     A printer log may be prepared in advance of a mission by enabling 
printer logging from the Set Options Menu (with the F10+F10 command), 
setting the desired simulation time (F8+F3 command), then starting the 
ground track display with ENTER; once the ground track has appeared on the 
screen, pressing the F key twice to set STSPLUS in the X60 fast time mode 
will generate the date relatively quickly (although the UT TIME printed may 
be off by as much as one minute in the X60 mode). Allow the simulation to 
run for the desired length of time, then press ENTER to return to the Main 
Menu. While the ground track is active Function Key F3 performs the same 
function as the F10+F10 command to enable or disable printer logging.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 112


SET DISPLAY FEATURES
--------------------

     Depending upon the satellite and personal preferences, a variety of 
display features may be enabled or disabled. Not all features are available 
with monochrome or CGA monitors. Pressing F3 on the Set Program Options and 
Features Menu will display the following menu:


                              Program STSORBIT PLUS

                  Space Shuttle and Satellite Orbit Simulation
                                  Version 9338

                   Current time:  19:59:10 PST   03:59:10 UTC
                   Current date:    02/24/1993     02/25/1993


         F1     ON      Display LOCAL Circles of Visibility
         F2     ON      Display TDRS and Real Time Satellites
         F3     ON      Display Additional Map Grid Lines
         F4     OFF     Display Tracking Stations
         F5     BOTH    Display Ground Track: DOTS/LINE
         F6     ON      Display Spacecraft Circle of Visibility
         F7     OFF     Display South Atlantic Anomaly Zone
         F8     ON      Display Terminator, SUN, and Spacecraft Lighting
         F9     ON      Display Map Locations and Features
         F10    ON      Display Lakes and Rivers

         ENTER          Return to MAIN MENU

         Select desired function:


F1     Display LOCAL Circles of Visibility
------------------------------------------

     Function Key F1 enables and disables the local circles of visibility, 
centered on your location and a second location (if enabled), and shows the 
approximate area within which direct line of sight communication with the 
satellite is possible. The circle is calculated at the instant the map is 
drawn and may not be accurate over long periods of time for satellites with 
highly eccentric orbits. In some situations (geosynchronous satellites, for 
example), these circles of visibility cover so large an area that they 
simply confuse and clutter the display. Use this command to disable the 
circles.


F2     Display TDRS and Real Time Satellites
--------------------------------------------

     This command provides a menu to display, modify, save, or read 
selected real time satellites and static satellites. The communications 
coverage for the Tracking and Data Relay Satellites (TDRS) or other 
geosynchronous satellites is also shown. The TDRS coverage boundaries 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 113


overlap between the East and West TDRS satellites and Mission Control may 
select either satellite during the overlap period. STSPLUS displays the 
areas covered by each satellite and the times for acquisition and loss of 
signal (AOS and LOS). See the section "TDRS and Real Time Satellite 
Features" above for a full discussion of the TDRS coverage features.


F3     Display Additional Map Grid Lines
----------------------------------------

     This command is not available for CGA systems. The basic world map 
includes the Equator and the meridians at 0 degrees (Prime Meridian) and 
108 degrees (International Date Line) shown in bright blue on color 
monitors. Turning on the map grid adds additional lines of longitude and 
latitude. Displaying the additional grid lines on some monochrome monitors, 
especially CGA, may make the screen too "busy".
     In the Orthographic, Quadrant and Zoom Map modes, the spacing of the 
additional grid lines is adjusted for the map field of view. In rectangular 
map modes (EGA and VGA systems only), each grid line is labeled at the left 
or bottom of the display screen.


F4     Display Tracking Stations
--------------------------------

     The F4 command enables/disables the display of the tracking stations 
included in file STSPLUS.TRK or the current TRACKING STATION filename as 
set by Function Key F7 on the Main Menu. If that file is not found, 
internal data are used for NASA's 14 original ground tracking stations plus 
the NASA Ground Terminal at White Sands, NM. Each tracking station is 
located with a small red circle. The circle of visibility is also shown if 
that circle has an angular diameter of 90 degrees or less. The circles of 
visibility are calculated at the instant the map is drawn and may not be 
accurate over long periods of time for satellites with highly eccentric 
orbits. For all map modes EXCEPT the World Maps, each tracking station is 
also labeled with its 3-character abbreviation. This command is not 
available for CGA monitors.


F5     Display Ground Track: DOTS/LINE
--------------------------------------

     STSPLUS calculates the ground track for the satellite for a period 
from one and one half hours in the past to three hours in the future. Press 
F5 to change from one mode to the next. Depending upon the user's 
preferences, this function may be used to set the displayed ground track to 
any of the following modes:

     NONE      The ground track is not displayed.

     DOTS      The ground track is displayed using RED dots for the past 
               ground track and GREEN dots for the future ground track. The 
               dots are spaced at one minute intervals. As time passes, the 
               GREEN dots will change to RED.


Program STSORBIT PLUS Satellite Orbit Simulation                   Page 114


     LINE      The ground grack is displayed using a GREEN line.

     BOTH      The ground track is displayed using a GREEN line with RED 
               dots for past ground track minute marks and YELLOW dots for 
               future ground track minute marks. As time passes, the YELLOW 
               dots will change to RED.


F5     Display Spacecraft Circle of Visibility
----------------------------------------------

     STSPLUS can calculate the approximate circle of visibility from the 
spacecraft, the area of the Earth's surface which is visible from the 
cockpit windows and television cameras or, for unmanned spacecraft, the 
direct line of sight visibility from the ground. Note that the shape of the 
"circle" varies depending upon the magnification or zoom factor and map 
projection being used. With rectangular projection, the shape is 
approximately a circle near the Equator and more like a rounded triangle at 
higher latitudes; near the poles, the "circle" spreads out across the map. 
This is an artifact of the rectangular map projection.
     When enabled, the circle of visibility is recalculated every 10 
seconds based upon the spacecraft's current altitude. This means that 
orbits with a high eccentricity (that is, a highly elliptical orbit whose 
apogee and perigee are very different) will exhibit a constantly changing 
circle of visibility.


F7     Display South Atlantic Anomoly Zone
------------------------------------------

     The South Atlantic Anamoly (SAA) is an area in the southern hemisphere 
lying between southern tip of Africa and South America which can cause 
severe electromagnetic disturbances on spacecraft. For example, the 
semiconductor memory on the Hubble Space Telescope (which regularly passes 
through the SAA) was being changed by this phenomenon until a patch was 
uplinked to work around the problem. The area is shown on the ground track 
as an ellipse for simplicity; its actual outline is more nearly shaped like 
a kidney bean. Using NASA Mission Charts for various Space Shuttle 
missions as a reference, the SAA is adjusted for spacecraft altitudes from 
160 nm to 350 nm (although it extends out to geosynchronous orbits).
     SAA coverage is disabled in orthographic modes pending better data and 
the development of a mathematical model for use in those modes.


F8     Display Terminator, Sun, and SpaceCraft Lighting
-------------------------------------------------------


     This function enables and disables the Sun and related solar features. 
See the section "Sun and Solar Features" for a full discussion. STSPLUS 
calculates whether the spacecraft is in full sun, penumbra (partial shadow) 
or refracted sunlight, or umbra (full shadow) and adjusts the color of the 
spacecraft icon accordingly: bright white, yellow, and dim white 
respectively. This feature is not available on CGA and HGC monitors. The 
current spacecraft solar lighting is indicated in the data block (next to 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 115


"Orbit #:") by the following symbols:

     *    Full sunlight
     +    Partial sunlight (penumbra)
     -    Refracted sunlight
          Full shadow (umbra)



F9     Display Map Locations and Features
-----------------------------------------

     This feature enables or disables the display of the map locations and 
features contained in file STSPLUS.LOC if present. See the section 
"Location and Features Labels" above for a full discussion.


F10    Display Lakes and Rivers
-------------------------------

     This feature enables or disables the display of lakes and rivers on 
the map. Removing the lakes and rivers will lessen the time required to 
draw a map and can improve screen legibility especially for CGA systems. 
(The lakes and rivers are always disabled on the rectangular world map to 
avoid cluttering an already busy display!)

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 116


STSORBIT PLUS's Orbital Model
-----------------------------

     The original version of STSORBIT was first prepared without reference 
materials of any kind and the simplest possible orbital model was therefore 
selected. The primary objective was to duplicate the NASA wall map at 
the Mission Control Center in Houston, Texas. This "simple" model assumed 
that the orbit was perfectly circular at a specified altitude and 
inclination which never degraded due to other factors such as drag or 
perturbation. Some simplifying assumptions were incorporated to handle the 
initial ascent portion of a mission and the launch site was hard coded to 
Cape Canaveral, Florida. With only minor modifications, the program was 
essentially unchanged for the next year.
     The launch of STS-31 and the Hubble Space Telescope highlighted the 
need for improved accuracy because of public interest and the length of the 
mission. The orbital calculations were modified (STSORBIT Version 9015) to 
include the J2 factor, the perturbation of low Earth orbits due to 
variations in the gravitational field related to the non-spherical shape of 
the Earth (among other factors); omission of the J2 factor caused errors in 
longitude of approximately -5 to -7 degrees per day. That is, the orbital 
track drifted Westward from its true position by that amount. More accurate 
models of low orbits also include the J3 and J4 perturbation factors, 
atmospheric drag, and a host of other less significant items.
     Although reasonably accurate for the first day or so of a space 
shuttle mission, the "simple" model is by no means ideal. In calculating 
the current orbital longitude, for example, the "simple" model assumes a 
circular orbit. For orbits with low inclinations, as is typical for 
launches from Kennedy Space Center, the errors are not particularly 
significant and are probably overshadowed by the fundamental uncertainties 
in orbital parameters and by the limitations imposed by display resolution. 
Orbits with higher inclinations, as would be the case if near-polar 
launches from Vandenburg AFB in California are ever initiated, would have 
much larger periodic errors which would be both noticeable and 
objectionable. More important for longer missions and for general satellite 
tracking is the fact that due to the method used, errors in the orbital 
calculations tend to be cumulative. After a day or two, the errors become 
unacceptably large.
     The real problem with the simple method, of course, is that the Earth 
is not a perfect sphere and actual satellite orbits are never perfectly 
circular. Satellite orbits are significantly perturbed by the non-spherical
gravitational field of the Earth, by the Sun and Moon, atmospheric drag, 
and other factors. Accurate satellite tracking over longer periods of time 
therefore demands more accurate data and a more rigorous treatment of 
satellite orbits. The only practical alternative is to use the NASA/NORAD 
2-line orbital element sets. Not only are these data readily available 
publicly, but they are relatively accurate and are updated regularly. 
Therefore, STSORBIT PLUS relies on the NORAD SGP4 prediction model and the 
2-line orbital element sets for orbit predictions. 2-line element sets for 
non-military space shuttle missions are typically available on the same day 
as the launch. Amateur astronomers and satellite tracking experts often 
generate "unofficial" 2-line element sets even for military missions.
     Six quantities are required by classical gravitational theory to 
completely characterize the orbit of one body about another in time and 
space, the "Two Body Problem". These six quantities, often referred to as 
Keplerian orbital elements, are included in the NASA/NORAD 2-line element 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 117


sets along with other numerical and statistical data. The U.S Space 
Command, (formerly NORAD, the North American Air Defense Command) 
headquartered in Cheyenne Mountain, Colorado, developed the SGP4 and SDP4 
orbital models and the 2-line element format many years ago as part of 
their satellite tracking efforts and NASA subsequently adopted the same 
format -- more or less. NASA and NORAD do not always use the same 
definition for revolution (orbit) numbers; NASA frequently gives a number 
one (or two) greater than NORAD, calling the first partial orbit number one 
while NORAD calls that same partial orbit number zero. Except for short 
duration missions, such as the Space Shuttle, revolution numbers are of no 
practical importance.
     Having timely and accurate orbital data is of little help without a 
computer model or program which can use those data. NORAD has rather 
arbitrarily divided satellite orbits into two categories: near Earth orbits 
and deep space orbits. Near Earth orbits are defined as those with orbital 
periods of 225 minutes or less and deep space orbits are all others. 
Computer models are described in the literature for each category. STSORBIT 
PLUS employs the SGP4 Near Earth Model only, using a composite of code of 
my own combined with translated Fortran and Basic source supplied by Paul 
Traufler and C source by Paul Hirose. I plan to add the SDP4 deep space 
model in due course. Not only are the near Earth orbits generally of more 
interest to observers, but the errors associated with deep space orbits 
processed with the SGP4 model (rather than the correct SDP4 model) are not 
particularly significant for the purposes of a program such as STSORBIT 
PLUS. Further, watching a geostationary satellite orbit on the screen is 
not unlike watching grass grow and is about as exciting.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 118


Accurate Time and the Personal Computer
---------------------------------------

     For a program like STSPLUS, accuracy and precision of the timekeeping 
functions are essential. There is a tendency these days to accept whatever 
a computer says as the absolute truth without regard for whether or not the 
information is even "reasonable". For something as basic as time, even an 
experienced computer user may assume that it is correct. This discussion 
attempts to compare reality with that expectation.
     Given the clock drift and accuracy problems inherent in the design of 
the typical IBM-compatible personal computer, frequent time setting and/or 
adjustments are required. Accurate time setting would not be practical 
for most people without the various time services provided by the National 
Institute of Standards and Technology (NIST) and the U.S. Naval Observatory 
(USNO). The NIST radio stations WWV and WWVH provide an inexpensive and 
convenient means for "ordinary folks" to synchronize clocks and other 
equipment. The NIST and USNO Telephone Time Services offer a high precision 
standard time calibration source when such accuracy is required. Similar 
radio and telephone services are available in Candad and Europe.
     Once a computer clock has been set with reasonable accuracy, the 
accuracy of the computer's clock will indeed be sufficient for many 
applications; if you are using a word processing or spreadsheet program, 
knowing the time to within a minute or two is probably adequate. For 
programs such as STSPLUS and other time-dependent applications, however, 
this level of accuracy simply will not suffice; when used for satellite 
tracking, the time should be accurate to within a second. Unless steps are 
taken to both set the clock and to maintain its accuracy, this will not be 
the case. No matter how accurately the clock on a typical personal computer 
is set, it will only be a matter of hours before the time will have drifted 
by some seconds. Measured over a number of days, the accumulated errors can 
easily amount to a minute or more.
     The timekeeping operations of an IBM-compatible computer are actually 
performed by two separate and independent functions: a clock-calendar 
CMOS integrated circuit and lithium battery combination which maintains the 
current time and date in hardware; and, a section of the DOS operating 
system software which maintains the current time and date in software. When 
computer power is off, the hardware chip continues to operate using its 
battery; when the computer is started ("booted"), the operating system 
software reads the hardware clock and sets its internal software clock. 
Absent special software, the DOS time thereafter relies entirely on the 
software clock until the next time the computer is restarted. 
Unfortunately, neither of these clocks was designed for accuracy; early 
versions of the PC did not even include the hardware/battery arrangement. 
Even the typical electric clock, which uses the power line frequency for 
its timekeeping reference, is usually far more accurate.
     The accuracy of the DOS time at any instant is the result of the 
accumulated errors in both clocks. The hardware clock will drift as a 
function of time, temperature, voltage, and crystal aging; the software 
clock will gain or lose time depending upon the skill with which its 
software was written and how well that software "cooperates" with the 
balance of the computer's hardware and software. Some software, especially 
network and high speed communications software, can prevent the DOS clock 
software from incrementing when it should, usually resulting in the DOS 
clock losing time. The problem was compounded with the release of DOS 
Version 3.3; beginning with that version, the DOS TIME and DATE commands 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 119


adjust BOTH the hardware and software clocks and thereby potentially 
eliminate the hardware clock as even a modestly reliable reference.


Methods for Setting DOS Time
----------------------------

     Bearing these considerations in mind, there are a number of approaches 
to the DOS time question. The most obvious approach, used by the vast 
majority of computer users, is to either ignore the computer clock entirely 
or to say "It's close enough". Regardless of the application, I strongly 
recommend that the DOS clock be REGULARLY set to the correct time if only 
to assure that files are more or less correctly date and time stamped. If 
the accuracy of DOS time is important, the computer clock may be set or 
synchronized in a number of ways, some of which are described below. In 
this context, "ACCURACY" means the accuracy of the time setting operation 
and NOT the longer term accuracy and stability of the DOS time.

1.   TELEPHONE: Many local telephone companies offer a telephone time 
     service, usually with a message such as "When you hear the signal the 
     time will be ... (beep)". I am not aware of any hardware or software
     which uses this signal for time setting purposes.

     ACCURACY: Generally plus or minus 5 seconds. With the advent of 
     digital voice response equipment in recent years, the accuracy has 
     improved to perhaps plus or minus 1 second.

2.   COMMERCIAL RADIO: Hourly time signals broadcast on commercial radio 
     may be used to manually set the time. My experience suggests that the 
     CBS network time signal is usually reliable.

     ACCURACY: Usually within plus or minus 2 seconds, depending upon the 
     source. Satellite distribution of network feeds add a time delay of 
     approximately 0.25 seconds per "hop" but some stations, including some 
     network stations, generate time signals locally.

3.   SHORTWAVE RADIO: Time signals are broadcast on shortwave radio 
     stations WWV and WWVH by the National Institute of Standards and 
     Technology. These time signals may be used to manually set the time. 
     WWV and WWVH broadcast on several frequencies: 2.5MHz, 5MHz, 10MHz, 
     15MHz, and 20 MHz (WWV only). Reception will vary according to your 
     distance from the transmitter, time of day, and atmospheric 
     conditions. These time signals are very precise; the only major 
     variable is the propagation delay, the time it takes the radio signal 
     to travel from the transmitter to your receiver. The typical 
     propagation delay is approximately 5 microseconds per mile. Outside 
     North America, other national radio services such as the British 
     Broadcasting Company's BBC World Service offer accurate hourly 
     shortwave time signals.

     ACCURACY: Time setting using WWV or WWVH can usually be performed to 
     within about plus or minus 250 milliseconds, of which up to 25 
     milliseconds is transmission time and the balance is user response 
     time. With practice, plus or minus about 100 milliseconds is 
     practical.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 120



4.   HEATH GC-1000 MOST ACCURATE CLOCK: The GC-1000 is a combination 
     digital clock and scanning shortwave radio receiver which may be 
     equipped with an RS-232 communications port for use with computers and 
     other electronic equipment. Operation with DC power is available to 
     maintain accurate time during periods of AC power loss. This is the 
     only method which provides more or less continuous accurate time 
     information without telephone toll charges.

     ACCURACY: When properly configured for your location, equipped with an 
     external antenna, used with appropriate computer software, and when 
     the receiver is locked to one of the WWV (or WWVH) time signals, the 
     GC-1000 can provide time information and a standard calibration 
     frequency to an accuracy of plus or minus 10 milliseconds. When signal 
     lock is lost, the receiver scans the 5MHz, 10MHZ, and 15MHz broadcasts 
     to reacquire signal and lock. Even after signal lock is lost, the 
     receiver maintains an accuracy of plus or minus 100 milliseconds for 
     some hours.

5.   NIST/USNO TELEPHONE TIME SERVICE: When real precision and accuracy are 
     required, the computer clock may be set remotely using the telephone 
     time service of either the National Institute of Standards and 
     Technology (NIST, formerly the National Bureau of Standards or NBS) in 
     Boulder, Colorado, or the U.S. Naval Observatory (USNO) in Washington, 
     D.C. This method requires a modem connected to a telephone line and is 
     available for systems using DOS version 3.3 or higher AND equipped 
     with 80286 processor or higher; some 8088-equipped systems may also 
     use this method depending upon the type of clock hardware installed 
     and the version of DOS being used. The recommended method uses the 
     programs TIMESET and RIGHTIME (see below) although other commercial 
     and shareware programs may be available.

     ACCURACY: This is the most accurate method available for setting and 
     maintaining the DOS clocks. Depending upon which service is used, NIST 
     or USNO, whether or not line delay compensation ("lag") is employed, 
     and the frequency of time setting, the DOS time can be set to within 
     plus or minus 2 milliseconds. However, since the "time ticks" of the 
     DOS software clock occur every 55 milliseconds, or 18.2 times per 
     second, this "granularity" may limit the accuracy of reading the DOS 
     clocks. See the documentation for programs TIMESET and RIGHTIME for 
     additional discussion.

     Choose one of the methods suggested or a suitable alternative based 
upon your precision and accuracy requirements. Other methods of maintaining 
an accurate time standard such as atomic clocks, Global Positioning 
Satellite (GPS) time receivers, and NIST time code equipment, are also 
available -- for a price. Those methods are beyond the scope of this 
documentation.


Maintaining Accurate DOS Time
-----------------------------

     Just in case you missed the point earlier, accurately setting DOS time 
is only half the battle. Even if the DOS time is set very precisely as 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 121


discussed above, all that assures is that the time is correct to the 
required accuracy at that instant. The problem then becomes one of knowing 
how the DOS clocks change or drift with time and how to compensate for 
those changes or, alternatively, checking the DOS time frequently enough 
that any drift on the part of the DOS clocks is acceptable for the intended 
application.
     Of the two clocks in a typical personal computer, the hardware clock 
is considerably more consistent and reliable. I have checked perhaps a 
dozen PC hardware clocks in recent years, and almost all kept reasonably 
good time over a period of several days; as expected, none kept "perfect" 
time. Typical drift rates ranged from about 3 seconds per day to near zero 
seconds per day, with the magnitude and direction of the drift more or less 
constant over the period of measurement. The hardware clock is typically 
sensitive to both voltage and temperature, both of which undergo 
significant change when the computer is turned on or off. Complete 
calibration of the hardware clock requires knowledge of its performance 
under both circumstances. Once a hardware clock has been calibrated, 
its performance may be predicted with reasonable accuracy over periods of 
some weeks or more. Crystal aging rates suggest that calibration should be 
performed at least monthly.
     The hardware clock is normally interrogated only when the computer is 
first started or rebooted. The correct time can therefore be predicted at 
that moment for a calibrated hardware clock, given the last time that clock 
was synchronized with an appropriate time standard. Microsoft provides no 
standard software tools for interrogating the hardware clock at other 
times except for low level interrupt services. Quite the contrary; 
beginning with DOS Version 3.3, using the DOS TIME and DATE commands to set 
the DOS software clock will also set the hardware clock and effectively 
destroy its usefulness as a calibrated time reference. I am at a complete 
loss to understand the reasoning behind this change in DOS; I presume that 
users were being "confused" by differences between the hardware and 
software clocks; instead of either explaining or fixing the problem, 
Microsoft elected to "legislate" the problem away -- a process any 
politician would recognize instantly. The only mitigating consideration is 
that any really effective solution would probably require hardware as well 
as software changes. Blame IBM, I guess.
     The software clock provides the only time information readily 
accessible to DOS using standard software. Since this clock is maintained 
entirely in software, with no reference to the hardware clock except at 
bootup, it is at the mercy of other software which may execute from time to 
time. The software clock increments its time using "interrupts", a 
technique which stops a software process in progress just long enough to do 
the required tasks and then resumes the interrupted process. These 
interrupts occur every 55 milliseconds. So long as none is missed, the 
software clock should keep accurate time -- if the software is written 
correctly and if the computer's crystal controlled oscillator is in turn 
accurate. It may be that neither of these conditions is true; certainly the 
crystal controlled oscillator (quite similar to the one which runs the 
hardware clock) was not designed for accuracy or stability. It's original 
purpose was solely to generate the necessary timing signals for the 
operation of the computer. Cost, not accurate time, was the primary 
consideration in its design.
     Other software designers have contributed to the problem by writing 
software which, deliberately or inadvertently, prevents the software clock 
from being updated. Off-brand BIOS firmware can present occasional 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 122


problems. Local Area Network (LAN) and high speed communications software 
are also frequent culprits in this respect. For example, a casual check of 
the clock while using a high speed computer-to-computer file transfer 
program indicated that the clock was effectively suspended when data 
transfers were in progress. In one relatively brief test, the DOS clock 
lost about 30 seconds.
     As a result of all of these factors, the accuracy of the DOS software 
clock can vary wildly from one computer to the next and from one situation 
to another. One inexpensive "clone" computer that I'd rather forget 
couldn't manage to keep time to better than about 30 seconds per HOUR! 
Before planning to use a particular computer as a time reference with 
programs like STSPLUS, check the computer hardware and software you intend 
to use very carefully.


Programs TIMESET and RIGHTIME
-----------------------------

     Two fine programs, TIMESET by Peter Petrakis and RIGHTIME by Tom 
Becker, provide all the features required to accurately set and maintain 
the computer's hardware and software clocks. Development efforts on these 
programs have been carefully coordinated so that they cooperate with each 
other. Both programs are copyrighted commercial software distributed as 
"shareware" and require registration after an initial evaluation period. I 
highly recommend these programs and encourage users to support the authors 
and their work. So far as I know, there are no other comparable programs 
available at any price!

TIMESET, Version 7.10 or higher, uses the telephone time services of NIST, 
USNO, and three European services to precisely set the computer clocks. The 
standard distribution also includes several additional time-related utility 
programs. It is available on many computer bulletin board systems or direct 
from:

          Peter Petrakis
          Life Sciences Software
          8925 271st N.W., Suite 112
          Box 1560
          Stanwood, Washington  98292  USA

          Telephone: (206) 387-9788

RIGHTIME, Version 2.5+, is a program to compensate for the various drift 
factors in a computer's hardware and software clocks. When used in 
conjunction with TIMESET and properly calibrated, RIGHTIME "learns" the 
warm and cool drift factors for a specific computer. As a result, the 
clock's can be maintained with an accuracy of a fraction of a second over 
long periods of time. It is available on many computer bulletin board 
systems or direct from:

          Tom Becker
          Air System Technologies, Inc.
          14232 Marsh Lane, Suite 339
          Dallas, Texas  75234  USA


Program STSORBIT PLUS Satellite Orbit Simulation                   Page 123


          Telephone: (214) 402-9660

Tom Becker and Peter Petrakis may be also contacted directly on the Air 
Systems Technologies computer bulletin board system in Dallas, Texas. The 
BBS always has the latest versions of TIMESET and RIGHTIME available for 
download:

          Air Systems Technologies BBS
          (214) 869-2780

     STSPLUS is now "aware" of program RighTime and its use is recommended 
for accurate timekeeping. Audible alarms in prior versions would perform 
unpredictably when RighTime was active because they use the hardware 
clock's timer functions (which RighTime also uses). STSPLUS now detects 
RighTime and temporarily disables RighTime while an audible alarm is being 
generated and then re-enables RighTime after the alarm has completed, 
restoring precise timekeeping. With RighTime active, alarms are generated 
in foreground, which may cause a slight delay in screen updating.


                               *************
                               *  CAUTION  *
                               *************

     STSPLUS expects RighTime Version 2.5+; performance with prior 
     versions of RighTime may yield unpredictable results. If using a 
     prior version of RighTime, do NOT enable audible alarms!


     If RighTime is not present or is not detected, the audible alarms are 
generated in background as in prior versions. This usually causes the loss 
of several clock ticks in the DOS software clock for each audible alarm. 
Although the time loss per audible alarm is very small, the cumulative 
error may become significant over extended time periods.

     The following descriptive text is extracted with permission from the 
documentation for the current versions of TIMESET and RIGHTIME; please 
consult the documentation for each program for full details. Although 
future versions of both programs are expected to remain compatible with 
STSPLUS, they should be tested carefully before regular use.


FEATURES OF TIMESET 7.10
------------------------

     TimeSet has been evolving steadily ever since the first version was 
released in the summer of 1987.  That version and several subsequent ones 
could only set a computer's clock from the U.S. Naval Observatory (USNO) in 
Washington, D.C.  Version 6.00, released in 1990, added ability to use 
telephone time signals from the National Institute of Standards and 
Technology (NIST) in Boulder, Colorado, making it the first program of its 
kind able to address more than one atomic time service.  This made it 
possible for computer users in the eastern and western United States to 
keep down long distance bills by choosing the time service closest to them.
     Version 7.10 continues that evolution with a number of new features 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 124


and supporting utilities:

o    TimeSet can now access five atomic clock-based telephone time services 
     on two continents: the USNO and the NIST in the United States, as 
     before, and atomic time services in Sweden (National Time and 
     Frequency Laboratory), Austria (Technical University of Graz), and 
     Italy (National Electrotechnical Institute).  People in European 
     countries who want to set their computers to an atomic clock no longer 
     need to make a trans-Atlantic phone call.

o    TimeSet 7.10 is designed to interact closely with version 2.5+ of 
     RighTime (tm), the excellent memory-resident regulator for computer 
     clocks developed by Tom Becker of Air System Technologies, Inc., 
     Dallas.  RighTime learns the drift rate in the computer's clock and 
     continuously applies a correction to compensate for it, and it refines 
     the correction each time the computer clock is set.  A computer with 
     RighTime installed and trained can maintain system clock accuracy 
     within a second for at least a week. Furthermore, version 2.46 
     provides true 0.01-sec resolution in the DOS clock, in contrast to the 
     normal 0.055-sec resolution.  This allows greater accuracy in 
     timesetting than ever before, indeed the maximum accuracy that can be 
     obtained with a computer clock.  Life Sciences Software and Air System 
     Technologies cooperated closely during the development of TimeSet 7.10 
     and RighTime 2.46, with the result that TimeSet can access several 
     RighTime functions directly. 

"TIMESET" is a trademark of Life Sciences Software (TM)

The following is a screen dump of the data displayed by TIMESET:

+------------------- From NIST.  Connect time: 11.97 sec. --------------------+
| DATA FOR TIME CALCULATIONS (all data pertain to Coordinated Universal Time) |
|    Time data string:  49051 93-03-05 14:07:20 81 0 -.1 051.1 UTC(NIST)      |
|                Date:  03-05-1993                                            |
|         Julian date:  2449051                                               |
|         Day of year:  064                                                   |
|                Hour:  14    Minute:  07    Second:  20                      |
|              The United States mainland is on standard time.                |
|        U.S. daylight time begins on 04-04-1993 at 02:00:00 local time.      |
+-----------------------------------------------------------------------------+
                                                System clock set: 06:07:20.01
+-----------------------------------------------------------------------------+
|                 ACTION SUMMARY (at instant of timesetting)                  |
|    Internal delay adjustment:  .01 sec. (added to set time)                 |
|        Line delay adjustment:  .0511 sec. (precompensated by time service)  |
|                                                                             |
|   Universal Time Coordinated:  14:07:20.01           (time at 0x longitude) |
|                     UTC Date:  03-05-1993, Friday    (date at 0x longitude) |
|                                                                             |
|      Local computer time was:  06:07:20.01 (RighTime-assisted)              |
|                       Set to:  06:07:20.01 Pacific Standard                 |
|      Local computer date was:  03-05-1993                                   |
|                       Set to:  03-05-1993, Friday, Day 064 of 1993          |
+-----------------------------------------------------------------------------+


Program STSORBIT PLUS Satellite Orbit Simulation                   Page 125



FEATURES OF RIGHTIME 2.5+
-------------------------

     RighTime brings exceptional system time of day clock performance to 
the DOS-based AT-class-compatible PC computer with no additional hardware.  
With RighTime installed, the standard real time clock system becomes an 
Adaptive Mathematically Compensated Crystal-controlled Oscillator based 
clock.  Under stable conditions, RighTime can produce a system clock that 
keeps time within one half second per week or better (some testers have 
reported accuracy of 0.07 second per week); this is about 0.8 parts per 
million error, or more than 100 times better than an unconditioned crystal 
time base alone, or 30 times better than a moderately conditioned one like 
a modern watch of quality.

o    True one hundredth second DOS clock resolution: the 55-millisecond 
     barrier is broken!  The standard DOS clock resolves to only about 1/18 
     second; under RighTime v2, the new high resolution DOS clock resolves 
     to, and increments in, hundredths while the Int 08h and 1Ch tick rate 
     remains standard. 

o    RighTime intrinsically sets the hardware clock and solves the midnight 
     rollover date bug that exists in some DOS versions; this eliminates 
     the need for other utility programs or drivers that perform these 
     functions.  Unlike DOS alone, the hardware clock seconds transition 
     will be properly set by RighTime and the time will be set to 
     hundredths of a second resolution, and these qualities will survive 
     through rebooting.

o    Each time you set the time, RighTime will improve the accuracy of the 
     clock error corrections and will subsequently improve the accuracy of 
     the clocks.  It should be easy to achieve a worst-case error of less 
     than 0.5 second per day and under good conditions, less than 0.5 
     second per week; typical results are much better.  Command line 
     options are provided that allow fine tuning the correction process to 
     your system.  A trimming option provides for offset adjustments in 
     hundredths of a second.

The following is a screen dump of the data displayed by RIGHTIME:

RighTime: Indicated DOS clock date and time is 1993/03/05 06:04:45.66.         
RighTime: Warm correction rate is +2.83 seconds per day.                       
RighTime: Cool correction rate is +4.27 seconds per day.                       
RighTime: Current applied DOS-CMOS RTC offset is +0.46 second.                 
RighTime: Last CMOS RTC adjustment was 0.00 hours ago.                         
RighTime: Last timeset was 23.33 hours ago.                                    
RighTime: System has been warm 17% of the time since the last timeset.         
RighTime: Stack A headroom is 92 bytes; Stack space used is 68 bytes.          
          Stack D headroom is 100 bytes; Stack space used is 60 bytes.         
RighTime: /?=Help; Version 2.53
RighTime: Copyright 1991-93 GTBecker, Dallas 214/402-9660. All Rights
          Reserved.
RighTime: Resident and enabled.                                                
RighTime: Selftest passed.                                                     

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 126


Computer Bulletin Board Systems
-------------------------------

     RPV Astronomy BBS        (310) 541-7299
     RPV Hotline BBS          (310) 544-8977
     CELESTIAL BBS            (513) 427-0764
     NASA GSFC OIG RBBS       (301) 262-6784
     NASA Spacelink BBS       (205) 895-0028
     CSS BBS                  (416) 458-5907
     JPL PAO BBS              (818) 354-1333

     Timely 2-line orbital elements are essential for accurate satellite 
tracking. In addition to my own bulletin board systems, five other bulletin 
board systems provide authoritatve data for the general public. Most files 
on these systems are compressed to reduce download time and must be 
decompressed before use.
     I maintain two computer bulletin board systems as a public service. 
The main system is the RPV Astronomy BBS at (310) 541-7299, 2400-14400 
baud. The backup system is the RPV Hotline BBS at (310) 544-8977, 1200-2400 
baud. During Space Shuttle missions, I post current 2-line elements at 
least daily (provided I'm in town!). Both systems usually also have current 
2-line elements for a large number of satellites in addition to other files 
of interest to space and astronomy enthusiasts. The systems are very 
popular and, therefore, are frequently busy!
     For the past several years, Major T. S. Kelso, USAF, has been making 
the US Space Command (formerly NORAD) orbital data available as a public 
service on his Celestial BBS at (513) 427-0674, 1 line at 1200 to 14400 
baud. The 2-line element sets are prepared by Kelso using data received 
directly from U.S. Space Command (formerly NORAD) by special arrangement. I 
regularly post a concantenated and sorted version of the current element 
sets on my own RPV ASTRONOMY BBS as file TLEnnn.ZIP, where "nnn" is the 
current Prediction Bulletin number. Kelso provides data for several 
categories of satellites:  Amateur Radio, Earth Resources, Manned 
Spacecraft, Navigation, Weather, and NASA's 30 Day Specials (which contain 
objects launched within the last 30 days and are often easy to spot 
visually). More specifically, these include the following satellites or 
satellite series: OSCAR, Radio Sputnik, UOSAT, Cosmos, LandSat, SeaSat 1, 
SPOT, Mir, Salyut 7, Soyuz, Space Shuttle, NAVSTAR (GPS), GOES, Meteor, and 
NOAA.
     The Canadian Space Society BBS, (416) 458-5907, 1 line at 1200 and 
2400 baud, also regularly posts NORAD 2-line elements. Much of the orbital 
data is obtained from Celestial BBS but additional data is generated by Ted 
Molczan and his worldwide team of observers. Note that the CSS format is 
slightly non-standard, having additional information on the first (title) 
line for each satellite, and may have to be edited for use with some 
tracking programs. The CSS files also have considerable additional text 
material (including current satellite news) before and after the actual 2-
line elements data.
     The U.S. Space Command sends all unclassified 2-line elements to the 
Orbital Information Group at Goddard Space Flight Center. These elements 
are available on the GSFC OIG RBBS, (301) 262-6784, 4 lines @ 1200 and 2400 
baud. (NOTE: The RBBS telephone number was changed effective July 24, 
1993!) The OIG database contains elements for some 7000+ satellites and is 
updated every weekday morning except holidays. Elements for popular 
satellites are posted in seven ".DAT" files (with the NORAD number only in 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 127


the first line of data rather than the more usual satellite name or IAU 
identification) and all other satellites are available on a query basis. I 
regularly post a combined and sorted set of the .DAT data as file 
GSFCnnn.ZIP on my own RPV ASTRONOMY BBS where "nnn" is a number like "269". 
Individuals who wish access to the RBBS must write (include full name and 
address):

          NASA Goddard Space Flight Center
          Project Operations Branch/513
          Attn: Orbital Information Group
          Greenbelt, MD  20771  USA

The OIG RBBS began operation in September, 1991. Until that time, the only 
method for obtaining the OIG data was by mail. OIG now plans to discontinue 
all mail services in early 1993 and thereafter the only method for 
obtaining the OIG data will be via the RBBS.
     The NASA SpaceLink BBS in Huntsville, Alabama, (205) 895-0028, 8 lines 
@ 300-9600 baud, provides mission information for all space shuttle 
missions and (usually) 2-line orbital elements both pre-mission and while a 
mission is in progress. 2-line elements for selected satellites are also 
available. In addition, SpaceLink has a wealth of other NASA information, 
computer programs, teaching materials, and image files.
     In January of 1993 the Public Affairs Office at the NASA Jet 
Propulsion Laboratory began BBS service related to JPL-supported missions. 
Mission status reports and high quality GIF images are the principal files 
currently available. The number is (818) 354-1333, two lines at 1200 to 
9600 baud.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 128


STSORBIT PLUS Revision History
------------------------------

      Each released version of STSPLUS uses a four digit revision code such 
as 9338. The first two digits indicate the year and the second two digits 
indicate the week of the year. In some cases, an additional letter suffix 
is added to distinguish changes occurring within the same week or to 
identify special versions. A partial week at the beginning or end of the 
year is counted as a full week. Using this method, a year will typically 
have 53 weeks although it is possible to have 54 weeks in a leap year (1972 
is an example). The current year-week revision code is shown on the Julian 
Date display, Display Mode 7, in my program ASTROCLK.
     This file records the revision history of program STSPLUS through all 
of the minor twists and turns that usually accompany the evolution of such 
a complex program. It illustrates the tortuous process of maintaining and 
refining a program as ideas and problems are reported from every quarter. 
These notes may also be helpful to users who are upgrading from one version 
to another to find out what has changed.

                                              David H. Ransom, Jr.


Version 9338 -- September 1993
------------------------------
-Repaired a bug in multi-satellite modes which caused a "trail of dots" to 
be left behind if the primary satellite icon fell on top of a secondary 
satellite icon (such as during close proximity operations).
-Repaired a bug when reading SCF files. In prior versions, the primary 
satellite was changed if the SCF file had a different primary satellite. 
The primary satellite in the SCF file is now ignored. The format of the SCF 
file is unchanged to maintain compatibility with prior versions.
-Modified the World and Zoom Maps in rectangular projection so that the 
PgDn key switches to Zoom Map (180 degrees) from World Map, and the PgUp 
key switches to World Map from Zoom Map (180 degrees).
-Added list of available .SCF files when reading, F6+F3 from the Main Menu.
-Added a warning when writing .SCF files if the requested file already 
exists. F6+F2 from the Main Menu. User must now press "Y" to overwrite an 
existing file, ENTER or any other key to cancel.
-By user request, modified the small character set (used for labels) to 
include the DASH ("-").
-After numerous user complaints, I've finally repaired the BLINK mode so 
that for most systems the primary satellite icon will blink on and off once 
per second. Press "B" while the map is displayed to toggle the BLINK mode.
-Repaired a minor bug which caused the message "Pause ... press ENTER" not 
to be displayed if the map was redrawn during Pause Mode.
-Thanks to the many users who took the time to carefully document these 
bugs, enabling me to find and fix them!


Version 9334 -- August 1993
---------------------------
-The maximum number of Static and Real Time satellites is increased to 32. 
This permits the entire GPS constellation, currently 25 active Block I and 
Block II satellites, to be tracked. The satellite setup display, F6+F1 from 
the Main Menu, has been modified to two display pages of 16 satellites 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 129


each; the second page of 16 is not displayed if no active satellites are 
present.
-Added "Clear Static and Real Time Satellites", F6+F4 from the Main Menu, 
to speed reconfiguration of these satellites. It may be used to clear any 
block of satellites NOT INCLUDING #1 AND #2 (which are assigned to TDRS 
East and TDRS West and must be cleared manually). Users are cautioned that 
once cleared, the satellite data for the cleared satellites is lost. If in 
doubt, save the current satellite configuration to a SCF file using F2 
BEFORE clearing!
-Somehow the "bullseye" was lost in the Tracking Mode for rectangular 
projection several releases back. It has now returned. Thanks to Alan Pound 
for reporting the problem!
-As an experiment, I changed the color of land boundaries from Light Cyan 
to Cyan to make multi-satellites and other display features a little easier 
to spot. Feedback welcome!
-When Extra Grid Lines are OFF (F10+F3+F3), changed the color of the grid 
lines from Light Blue to Blue and added lines of latitude at +80 and -80 
degrees.
-Various repairs to eliminate spurious pixels and other minor problems 
associated with multi-satellites.


Version 9333 -- August 1993
---------------------------
-This is a MAJOR UPGRADE, adding multi-satellite capability. This is the 
first in a series of upgrades for tracking multiple satellites and 
rendezvous missions. Comments, suggestions, and bug reports are welcome!
-Special thanks to Joel Runes for his assistance during beta testing!
-OPERATIONAL HINT: With the addition of multi-satellite tracking, the 
Motion Map feature now really comes into its own; press "M" when the normal 
map is displayed to switch to the EGA Motion Map, press "M" or ENTER to 
return to normal map or to the Main Menu. All satellites are updated as 
fast as the computer can draw the map. See the notes on a "vanilla" boot 
without memory managers for dedicated STSPLUS uses.
-The format of file STSPLUS.INI has been substantially modified and files 
from prior versions of STSPLUS will be ignored. The configuration 
information must therefore be re-entered.
-Increased to sixteen the number of additional TDRS and real time satellite 
positions in file STSPLUS.INI so that all active satellites may be updated 
and displayed. Sample data are shown below. See the section "TDRS and Real 
Time Satellite Features" for additional information.

     19883,"TDRE ", -0.04218, -41.14169,10014
     21639,"TDRW ", -0.03643,-174.14074,10014
     22314,"TDR5 ", -0.31155,-138.36021,10004
     19548,"TDR2 ",  0.05352, -61.66467,10004
     13969,"TDR1 ", -6.59117,-170.55876,10004
     16609,"MIR  ",-17.45706,-178.73251,14115

-TLEs for each active satellite are now saved in the .INI file so that 
accurate positions may be calculated dynamically. These TLEs should be 
updated periodically.
-TLEs are may now also be saved in and read from special .SCF (Satellite 
Configuration File) files so that multiple TDRS and Real Time satellite 
configurations may be saved and/or selected. A sample file, STSPLUS.SCF is 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 130


included in the standard distribution. Function Key F6 from the Main Menu 
is used to display, modify, save, or read these data.
-The 5-character abbreviation of each TDRS satellite may now be used to 
label the satellite. The size and color of the icon used to display each 
TDRS or real time satellite may now be independently controlled.
-STSPLUS now uses the calculated LATITUDE for the display of all TDRS 
satellites. This will cause TDRS1, for example, to appear up to 7 degrees 
North or South of the Equator (as of 8/9/93).
-The drive, path, and name of the .CTY file may now be set with F7 from the 
Main Menu.
-The Motion Map is now available for the World Map in rectangular 
projection. This is helpful with multiple real time satellites.
-Repaired an infrequent bug discovered by Joel Runes which causes the 
orthographic map to be redrawn continuously when a) the satellite has a 
high eccentricity (.73 in the test case), and b) when the map is being 
drawn at approximately the time of perigee. The code has been modified to 
take the Eccentricity into account in calculating the map offset time.
-Corrected a minor bug which caused MET in excess of 9999 days to overflow 
the assigned format statement for the data block and appear as 
"%12038/00:00:00 MET" with the "MET" wrapping around to the left side of 
the screen. Obviously, there aren't many satellites with this problem, but 
NORAD #00051 is one such. The STSPLUS.LTD entry for this satellite is:

     00051,2437158.90208333,0

and the problem was noted because of the pre-launch "temporary" NORAD 
number assignment for STS-51.
-A similar problem occured with the large clock displays. In both 
projection modes, only the last four days of MET are now displayed (12038 
days will display as "2038").
-Added a reminder in the text that when entering filenames using F7 from 
the Main Menu, a drive and path may also be included if desired. That 
capability has been present for some time but was not stated explicitly.
-Changed the precision that the "plain English" display of the elements 
Epoch Time is displayed for approval (F2 from the Main Menu) from [rounded] 
integer seconds to 0.001 seconds, coordinated with VEC2TLE V9331.
-Several V9332 Beta Versions were released privately for testing.


Version 9331 -- July 1993
-------------------------
-In coordination with Ken Ernandes' VEC2TLE, the data output for Format 7,
ECI State Vector (Labeled Data), has been modified. The data have been 
supplemented by the addition of two lines: Element Set Number; and, Rev 
Number at Epoch. The IAU Designation has been added to the Catalog Number 
line and the Epoch Time is now given to .001 seconds. The data output for 
Format 4 has been changed so that it is identical to Format 7. See text for 
details.
-Per Ken Ernandes, the Format 4 & 7 label "Ndot/3" is changed to "Nndot/6".
-I have received NO REPORTS from anyone using Data Formats 5 and 6. Those 
formats may not continue to be supported indefinitely UNLESS I am informed 
of applications which use them.

     CAUTION: STSPLUS Version 9331 Data Formats 4 and 7 are NOT compatible 
     with VEC2TLE Version 9322 when multiple state vectors are generated! 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 131


     Use a release of VEC2TLE with a version number equal to or greater 
     than 9331. (However, manually editing the data to remove the Elset and 
     Rev Number lines can restore compatibility with the older version.)

     NOTE: Users are urged to update to VEC2TLE Version 9331 or the current 
     version, which ever is later! Not only does the current version of 
     VEC2TLE maintain compatibility with STSPLUS but several important new 
     features have been added and a bug in Version 9322 which affected data 
     accuracy under certain circumstances has been repaired.

-The Tracking Station Mode is now active in both Orthographic and 
Rectangular projections. The projection used will same as the one which is 
active when the "T" key is pressed.
-Repaired a bug which caused the NORAD number displayed in the Pass 
Prediction Mode to be incorrect under certain circumstances. Thanks to 
Grant Pinto!
-Repaired a bug in the pass prediction logic which caused the MAX 
VISIBILITY data to be missstated by a significant amount for certain 
satellites, especially ones with higher eccentricities. Thanks to Grant 
Pinto for spotting and reporting the bug!
-Changed the default time zone abbreviation for unrecognized (foreign) time 
zones from all spaces (which confused the Pass Prediction setup!) to "LCL".
-Corrected a bug using F2 from the Main Menu which showed no 2-line 
elements files if no .TXT files were found in the current directory but one 
or more .TLE files were present. Thanks to Bob Krohn for reporting the bug. 
If no files of either filetype are found, an error is displayed and the 
user is returned to the Main Menu.
-Corrected a bug in default paths if the root directory was used. (Path 
defaulted to "B:\\" instead of "B:\" for drive B:, etc.)
-Corrected a bug in the NORAD number for F2 from the Main Menu. If the 
NORAD number was greater than 32767, a negative nunber was shown.
-Disabled RIGHTIME detection for 8086/8088 processors. The detection 
process affected the time in certain XT-class machines.
-Corrected a minor bug which caused the "blink" feature for the satellite 
icon not to function under certain circumstances.
-Corrected a minor bug which initialized the Location Flag incorrectly for 
CGA systems when file STSPLUS.INI was not present. Locations and Features 
were displayed even though the menu display indicated they were OFF.
-Various cosmetic changes.
-Most of the changes in this release were included in Beta Version 9329.


Version 9320 -- May 1993
------------------------
-This is a MAJOR UPGRADE, adding new improvements and features along with 
high precision state vector data output for use with Ken Ernandes' program 
VEC2TLE.
-By popular request, STSPLUS now estimates if a satellite may be visible to 
the naked eye or binoculars, and displays "VIS" in bright white next to the 
orbit inclination if a visual sighting may be possible. See the section 
"Satellite Visibility" for additional discussion.
-Also by popular request, the pass predections (F3, Data Mode 9) have been 
enhanced to permit dates and times to be displayed for either UTC/GMT or 
LOCAL time. An additional prompt has been added for that selection.
-When displaying predicted passes (F3, Data Mode 9), the satellite is now 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 132


approximately centered in the display (instead of being well to one side).
-After considerable confusion and several user comments, I have reworked 
the pass prediction logic so that when the user returns to the Main Menu 
after the ground track for a predicted pass is displayed, the time is 
automatically restored to the real or simulated time in effect BEFORE the 
pass prediction was displayed. This means that repeated use of the pass 
prediction feature will generally display the same list of numbered passes 
and the user no longer needs to restore real time (or reset simulated time) 
after displaying predicted passes.
-Corrected a cosmetic bug on pass predictions when an illegal pass number 
(greater than the last pass number displayed) was entered at the prompt.
-Added an asterisk ("*") at the left of each event timer when the satellite 
is AOS (signal/Sun is being received). This will particularly benefit users 
with monochrome or shades of gray.
-Enhanced the Precision X-Y-Z State Vector Data Modes (F3, Data Modes 4 
through 7) to include four output formats: multi-line Ascending Node with 
state vector, 2 numeric data lines, comma delimited, and multi-line labeled 
data. State vectors may now be logged continuously, for a specific time, or 
for a specified time span. See text for details.
-Corrected a problem with state vectors being generated at the wrong time 
(Data Modes 5 through 7) when the time was entered in UTC and local time 
was a different date.
-Removed the low precision state vector data output (F3, Data Mode 4).
-Changed the angle used to calculate the Earth's partial penumbra from 1.2 
degrees to 0.3 degrees to better correspond with observed lighting. The Sun 
AOS and LOS penumbral calculations were also slightly adjusted; timings 
during STS-56 indicated about a 15 to 20 second error before these changes.
-Updated the TDRS information in the section "TDRS Satellite Features" and 
all five TDRS satellites are now displayed on the maps at their approximate 
locations as of 05/05/93. Thanks to Jim Walls for reminding me!
-Corrected a bug which caused "BASIC Error = 5" when the selected satellite 
had probably decayed. #22209 MIR Debris was an example in file TLE180.TXT. 
STSPLUS now displays a warning message if the satellite has a current 
altitude less than 75 nautical miles and then returns to the Main Menu.
-Corrected the conversion from kilometers to feet per Ken Ernandes. (My 
original conversion factor was taken from a 40+ year old Handbook of 
Chemistry and Physics and was very slightly in error!)
-Repaired (I think...) a truncation problem which sometimes caused MET/T+E 
to run one second slow.
-For all those who refuse to read documentation, I added a reminder to the 
Main Menu: "WHILE MAP IS DISPLAYED: F1 = HELP, ENTER = Main Menu".
-Special thanks to Ken Ernandes, Joes Runes, and Willie Musty for state 
vectors, testing, and validation of the new features in recent versions!
-Version 9319 was released privately for beta testing.


Version 9316 -- April 1993
--------------------------
-This is a BETA MAINTENANCE UPDATE not released publicly.
-Added Data Output Function #5, "Precision XYZ State Vector (km)", to 
generate full precision state vectors. The position and velocity data are 
in km and km/sec. The format is similar to Data Output Function #4 except 
that it requires two data lines per state vector.
-Help is now available in all display modes by pressing Function Key F1. 
Press F1 again to return to normal data display.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 133


-The default (and minimum) magnification for the End key in orthographic 
modes has been changed from 100 to 150. Thus, pressing the End key will 
return to the prior magnification or to MAG=150, whichever is greater.
-Added missing minus sign on large character MET during the last 24 hours 
prior to launch time. Display was "0/00:01:00" instead of "-0/00:01:00".
-Corrected the latitude for Mauritius in file STSPLUS.LOC. The latitude was 
missing a minus sign! Changed the "trigger" magnitude for Athens, Greece to 
500 from 2000 following a user complaint. Also corrected the longitude for 
Luxor, Egypt which was off just that little bit ...
-Various minor cosmetic changes.


Version 9314 -- March 1993
--------------------------
-This is a MINOR UPDATE to correct several problems. Except for these 
notes, the documentation is essentially unchanged.
-Corrected a bug with F6 on the Main Menu. Switching between MET and T+E 
using F6 changed the label but NOT the data. (F5 worked correctly when the 
ground track is displayed.) Thanks to Paul Ferrante for reporting the bug.
-Corrected (again!) a format error in file STSPLUS.OBS which is created for 
use with TRAKSTAR. For names shorter than 20 characters, the numerical data 
was shifted left. Thanks to Michael Simmons for helping track down the bug!
-Corrected the CPU identification displayed for 386 processors to "80386DX 
or 80386SX". Due to a typo, the SX processor was shown as "80387SX".
-Corrected the spelling of Yarragadee, Australia. Thanks to Elwood Marshall 
for the correction.


Version 9311 -- March 1993
--------------------------
-This is a FULL RELEASE with updated documentation, and includes all 
changes listed here as well as those made in Preliminary Versions 9307 
through 9310. Please see the update notes below for details.
-Added F1 to the Main Menu, Convert Keplerian Elements to 2-Line Format, 
which incorporates the features formerly provided separately in my program 
MAK2LINE. See new text for discussion and for a form which may be used to 
transcribe data received by voice or modem.
-Repaired a bug which caused the Location Map isocontours to be drawn at 
the wrong location when a second location was enabled in orthographic mode. 
Thanks to Paul Ferrante for reporting the problem!
-Added Function Key F9 to the Time and Date Menu (F8 from the Main Menu) to 
show the last system TIMESET and the current RIGHTIME corrections. This 
menu item will not appear if program RIGHTIME is not detected.
-Added additional code to maintain the prior state of RIGHTIME per Tom 
Becker. Thanks, Tom!
-Various minor cosmetic changes.
-Documentation updated.


Version 9310 -- March 1993
--------------------------
-This is a MAINTENANCE UPDATE and also includes several improvements to 
Version 9309. Users updating from Version 9250 should also read the notes 
for Version 9309 below.
-In my rush to release Version 9309 of STSPLUS prior to STS-55, I neglected 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 134


to finish updating the code for F2 (Read 2-line elements). Hopefully, that 
code has now been repaired correctly ... sorry!
-STSPLUS is now "aware" of program RighTime by Tom Becker. Audible alarms 
in prior versions would perform unpredictably when RighTime was active 
because MS BASIC uses the hardware clock's timer functions for "music" 
(which RighTime also uses). STSPLUS now detects RighTime and temporarily 
disables RighTime while an audible alarm is being generated and then re-
enables RighTime after the alarm has completed, restoring precise 
timekeeping. With RighTime active, alarms are generated in foreground, 
which may cause a slight delay in screen updating.
-CAUTION: STSPLUS expects RighTime Version 2.5+; performance with prior 
versions of RighTime may yield unpredictable results. If using a prior 
version of RighTime, do NOT enable audible alarms!
-If RighTime is not present or is not detected, the audible alarms are 
generated in background as in prior versions. This usually causes the loss 
of several clock ticks in the DOS software clock for each audible alarm. 
Although the time loss per audible alarm is very small, the cumulative 
error may become significant over extended time periods.
-Added the flashing message "calculating ..." during Pass Prediction 
calculations so that users with slow computers (especially those without a 
math coprocessor) will know that the process is continuing. Users with 286 
computers and no math coprocessor report delays up to tens of minutes for 
satellites with low mean motions!


Version 9309 -- February 1993
-----------------------------
-This is a PRELIMINARY RELEASE of a major update for STSPLUS and the first 
public release since Version 9250. This version is being released as an 
UPDATE ONLY for Versions 9250 and 9307; the full version will be released 
shortly, complete with full documentation, pending the results of testing 
for this preliminary release. See also the update notes for Version 9307 
below. Comments and suggestions are invited, particularly with respect to 
the new Data Output and Pass Prediction features.
-Function Key F3 on the Main Menu, Pass Predictions and Data Output, has 
been rewritten and improved.
-Added Line-of-Sight Pass Predictions for the current satellite. Use F3 
from the Main Menu and select Data Format 9. Pass predictions are made for 
48-hour blocks and for up to 99 passes. Users may immediately display a 
listed pass by entering the pass number. STSPLUS then automatically sets 
SIMULATED TIME to the middle of the pass and switches to the ground track 
display. See the section "Pass Predictions and Data Output" for additional 
information. The capability to use TRAKSTAR or other external tabular pass 
prediction software has been retained for those who prefer that technique.
-Improved and refined the Data Output capabilities introduced in Beta 
Version 9307. Added FILE Data Output to file STSPLUS.LOG, and PRINTER Data 
Output to printer LPT1:.
-Modified F2 on the Main Menu (Read 2-line Elements) to require the "#" 
symbol when entering the NORAD number; enter the NORAD number as "#20580". 
This now permits satellite names such as "1993 012A" to be found correctly; 
prior versions would treat such an entry as a NORAD number and the search 
would fail.
-Entering a full drive and path specification in addition to a filename 
with F2 on the Main Menu (Read 2-line Elements) will now correctly set the 
path without the need to use F7 (Set Paths and Filenames). Root directories 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 135


("C:\") are now processed correctly. Press ESC to cancel.
-Added text section titled "Time and the Personal Computer" which offers 
information on setting and maintaining the PC clocks over long periods of 
time. Includes information on programs TIMESET and RIGHTIME.


Version 9307 -- February 1993
-----------------------------
-This is a BETA TEST VERSION, not released publicly.
-Added Function Key F3 to the Main Menu. This provides data output on the 
selected COM port with specified data items. Three different data formats 
have been implemented so far.
-Removed the original Function Key F3 (Read .INI file) from the Main Menu. 
Use F2 to read 2-line elements and/or set file names. In Version 9250, the 
satellite data was not being read when the .INI file was changed. This was 
caused by logic changes to speed up initialization of the program. Also, 
reading "foreign" .INI files sometimes caused problems.
-Corrected a bug which caused a new launch time/date NOT to be added to 
file STSPLUS.LTD if the curret satellite's NORAD number was less than the 
last NORAD number in the file.
-In response to a request by Maj. T.S. Kelso, USAF, who prepares the 2-line 
orbital elements which I post on my RPV ASTRONOMY BBS, I have changed the 
name of that file from "NASAnnn.TXT" to "TLEnnn.TXT". The default file 
which STSPLUS looks for has been similarly changed. Since the orbital data 
in the file does NOT come from NASA but from US Space Command, the use of 
"NASA" in the filename was confusing and did not give credit where it was 
due.
-Corrected a minor bug which caused five pixels to be restored incorrectly 
under the starbord (right) wing of the space shuttle icon.
-Modified the operation of Function Key F5 from the Main Menu to ADD or 
UPDATE new launch time and date in file STSPLUS.LTD rather than to append 
the new data at the end of the file. This assures that the satellite is 
included only once in the file and that the new or updated information is 
always read correctly. Prior versions required the user to manually edit 
the file to remove multiple entries.
-Adjusted the maximum angle displayed for the isocontours (concentric 
circles of satellite visibility) on the Location Map in orthographic mode 
to take satellite altitude into account.
-Corrected the STSPLUS.OBS file format for use with TRAKSTAR. The data was 
correct but the spacing caused TRAKSTAR to sometimes read the data 
incorrectly. Thanks to Michael Simmons for reporting the problem!
-Corrected the latitude of Sao Paulo, Brazil in file STSPLUS.LOC. It was 
one degree off to the South and wound up in the Atlantic Ocean ...


Version 9250 -- December 1992
-----------------------------
-This is a MAINTENANCE AND FEATURES UPDATE.
-In response to numerous suggestions, I have redesigned and enlarged the 
space shuttle icon and switched from a profile to a plan view to make the 
icon easier to find on the screen. The new icon has almost three times as 
many pixels and takes more time to draw. Comments are invited!
-In response to many user requests, I have improved file selection logic 
for 2-line elements using F7 from the Main Menu to "remember" the path and 
save it in file STSPLUS.INI. Users may now keep all 2-line elements files 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 136


for STSPLUS and other tracking programs in a separate directory.
-While the default filetype for 2-line elements is still ".TXT", the 
program now also searches for filetype ".TLE".
-Event timers (showing AOS and LOS for the local station, TDRS, etc.) are 
now enabled by F10+F7 from the Main Menu.
-I have added the Location Map in orthographic mode; press "L" while an 
orthographic map is displayed. The projection used for the Location Map is 
now based upon the current projection, rectangular or orthographic, when 
"L" is pressed.
-Improved resolution of spacecraft lighting from 10 seconds to 1 second and 
the Sun's position is now calculated every 10 seconds instead of every 60 
seconds.
-Spacecraft lighting icon and symbol (to the right of "Orbit #:" in the 
data block) now indicate the full range of solar illumination:
     *    Bright White   Full sunlight
     +    Yellow         Partial sunlight (penumbra)
     -    Light Red      Refracted sunlight
          White          Full shadow (umbra)
Note that LIGHT RED and the "+" and "-" symbols have been added to 
distinguish refracted sunlight from partial sunlight.
-In response to several user requests, I have added AOS and LOS event 
timers for orbital sunrise and sunset, displayed when the solar features 
are enabled. In order to avoid excessive delays during the ground track 
plotting (when the timers are set up), I have used a simpler algorithm for 
orbital sunrise and sunset than that used during program operation. The 
simpler algorithm is usually accurate to about plus or minus 15 seconds. 
The actual spacecraft lighting is calculated dynamically and is both more 
accurate and takes into account the non-spherical shape of the Earth.
-After several user comments about the "big clocks", I have again tweaked 
the shape of the large digit "5" (back to what I started with) and modified 
the "6" to better distinguish it from the "5".
-In order to free a display line in orthographic mode, the map drawing time 
and map database file information have been combined on a single line (e.g. 
"EARTH4  10.91") at the bottom of the display block.
-STSPLUS now automatically detects the type of processor and math 
coprocessor; if no math coprocessor chip is detected, the program displays 
a caution message at startup. The SLOW MODE is now automatically set or 
reset depending upon the presence or absence of the math coprocessor and 
the menu selection for the SLOW MODE has been removed.
-Performance may be improved if a memory manager such as EMM386, QEMM386 or 
386MAX is NOT used! See the section "PROGRAM SETUP AND USAGE NOTES" for 
specific information.
-Changed the grid spacing in orthographic mode, MAG=200, to 10 degrees from 
5 degrees to make the display a bit less cluttered.
-STSPLUS is now compiled using Microsoft Visual Basic for DOS.
-Updated this documentation. Added the sections "SUN and Solar Features", 
"Event Timers and Audible Alarms", and "F5  Display Ground Track: 
DOTS/LINE". Moved the section "F5  Show Ascending & Descending Node Data" 
to the proper place in the text.
-Corrected a bug which caused a minus sign (if present on Y or Z) to 
persist when changing from XYZ to Alt/Az or RA/DEC satellite coordinates.
-Various minor cosmetic changes.
-Version 9249 was a limited release beta version.

Version 9245 -- October, 1992

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 137


-----------------------------
-This is a MAINTENANCE UPDATE, correcting several bugs and adds the launch 
date and time capability.
-Added file STSPLUS.LTD which contains the NORAD number and launch date 
(Julian date, UTC) for selected satellites. A sample entry appears as:

     22194,2448918.21503472,0

This example is the data for Space Shuttle mission STS-52 (NORAD #22194) 
and corresponds to a launch date and time of 22 OCT 1992 @ 17:09:39 UTC. 
The last parameter is reserved and should be set to zero. Launch date and 
time may be appended to file STSPLUS.LTD when entered using F5 from the 
Main Menu. See the section "Using File STSPLUS.LTD for Launch Date & Time" 
for a complete discussion.
-Corrected a misplaced statement which caused "BASIC PDS Error = 5" when 
the Satellite Motion Map was requested from rectangular modes.
-Changed future dots on ground track to LIGHT GREEN when only dots are 
shown to avoid confusion with solar terminator. (That's what it was 
supposed to be but I messed up ...)
-Changed satellite circle of visibility on the Satellite Motion Map to 
solid white (from light white dots) for greater clarity.
-Added a default magnification of 200 for the End key.
-Corrected the coordinates for Shanghi, China, in STSPLUS.LOC.


Version 9244A -- October, 1992
------------------------------
-On rectangular projections, the LAUNCH TIME and LAUNCH DATE were shown 
incorrectly. The calculations for MET were correct. 


Version 9244 -- October, 1992
-----------------------------
-Version 9244 is a MAINTENANCE UPDATE which adds several new features in 
addition to repairing a number of bugs which have been discovered as a 
result of the addition of the orthographic map mode and other new features 
such as enhanced TDRS coverage. This is still "early in the game" following 
the major rework associated with the addition of orthographic projection. 
Comments, suggestions, and bug reports will be appreciated.
-Added EGA dual-page Satellite Motion Map to orthographic modes, available 
ONLY for EGA and VGA systems. Press "M" while the orthographic map is 
displayed. Press "M" or ENTER to return to normal map modes. PgUp, PgDn, 
Home, and End are the only other keys which are active with the Satellite 
Motion Map.
-In response to MANY requests, I have restored the "red dots" for past 
orbital ground track. (My original method no longer worked when I added the 
orthographic projection.)
-AOS/LOS for secondary location now available in orthographic mode and in 
rectangular mode with "/CLK" command line option AND when large clock is 
selected for MET/T+Epoch (using F2 when the map is displayed). Finding 
display space is getting very difficult, particularly in normal rectangular 
modes! Primary location is labeled "STN1" and secondary location is labeled 
"STN2".
-The PAUSE mode has FINALLY been repaired so that it operates correctly. 
Press F6 while the map is displayed to enter PAUSE, press ENTER to resume 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 138


normal operation. Use the "+" and "-" keys to advance or retard the time, 
and use F4 to set the time step. See the section "Pausing the Ground Track 
Display" for a full description.
-The FAST mode has also been repaired so that it works more or less in the 
manner intended. Press F4 while the map is displayed to enter FAST mode. 
Note that the actual time increment is a function of the computer's speed. 
For fast computers, the time increment will usually be 10 or 60 seconds but 
may vary by a second occasionally; for slower computers, the time increment 
may be somewhat longer. See the section "Using FAST Time" for a full 
description.
-Corrected a problem with TDRS coverage when updating from one version to 
another. The TDRS AOS/LOS labels read ":" instead of "TDRE:" and "TDRW:" 
and the AOS/LOS calculations could be incorrect or blanked out. (The TDRS 
data were not being set up correctly.) As a work-around, the problem could 
be corrected by deleting file STSPLUS.INI and restarting the program.
-Corrected a crash with "BASIC PDS Error 5" which occurred under certain 
circumstances when drawing circles of visibility in orthographic mode. (An 
array index was being overrun.)
-Corrected a minor bug in the AOS/LOS logic that limited the time 
resolution to 2 seconds instead of 1 second (4 seconds instead of 2 seconds 
when the SLOW flag is set). Thanks to Joel Runes for spotting the problem!
-Various minor cosmetic bugs.

NOTE:     Version 9243 was a beta version released on a limited basis to 
          individuals who had problems and/or registered the program 
          immediately before and during Mission STS-52. Version 9243 
          included some of the changes noted above for Version 9244.


Version 9242 -- October, 1992
-----------------------------
-Version 9242 is primarily a Maintenance Update, correcting a number of 
minor bugs and documentation errors. However, several "new and improved" 
features have also been added as a result of continued testing and user 
requests. Thanks to everyone who sent in encouragement and suggestions!
-In response to MANY user requests, I have added an interface (via F4 from 
the Main Menu) to TS Kelso's new satellite prediction program TRAKSTAR. 
Download TRAKSTR2.ZIP (filename for Version 2.15) from RPV ASTRONOMY BBS or 
from Celestial BBS (see text for telephone number). CAUTION: TRAKSTAR uses 
UTC time rather than LOCAL time! See text for full description and setup 
instructions.
-By popular request, I've added an audible warning for AOS and LOS at the 
user's location. The AOS warning occurs 2 minutes prior to AOS, and the LOS 
warning occurs 30 seconds prior to LOS. Audible warnings are enabled and 
disabled using F10+F8 from the Main Menu. Past versions of Microsoft's 
compilers have caused the system clock to lose time when "music" was 
played; I would appreciate feedback from users if this feature causes 
problems.
-A similar (but shorter) audible warning has also been added for TDRS 
coverage. The TDRS warnings occur 30 seconds before AOS or LOS if TDRS 
coverage and audible alarms are both enabled.
-AOS and LOS clocks now change to YELLOW if the time is 2 minutes or less, 
as stated in the documentation. A minor bug has been repaired that caused 
the AOS or LOS clocks to sometimes "freeze" at 00:00 or 00:01 when no 
future event was detected.

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 139


-AOS and LOS calculations have been improved in precision by a factor of 
two and the average time required for the calculations has decreased by 
about 5:1 using a binary search algorithm. This may be just an exercise in 
performance improvement since factors such as antenna pointing errors and 
atmospheric conditions may introduce errors of up to tens of seconds!
-When launch time and data have been entered and Mission Elapsed Time is 
selected for display, the HOURS:MINUTES for MET will appear at the bottom 
of the data block in large digits for orthographic modes. (When MAG is 
greather than 100, seconds are not displayed because of space limitations. 
The full MET, including days, is always displayed near the top of the data 
block in normal characters.)
-Corrected error when changing to/from DAYLIGHT TIME using F8+F10 from the 
Main Menu. If the Daylight setting is changed, STSPLUS now asks if you wish 
to adjust your DOS clock. CAUTION: Setting the DOS clock may NOT execute 
correctly for 8088 computers! (Prior versions required exit from the 
program and restart before the time was shown correctly.)
-Corrected the satellite coordinates when orthographic mode was selected 
with the second city displayed. (V9240 displayed the primary location name 
but the data for the secondary location.)
-Corrected a problem (which left the screen black most of the time and then 
was redrawn immediately) when Motion Map was requested (by pressing "M") 
from other than Zoom Mode.
-Corrected TDRS AOS/LOS title placement error with "/CLK" command line 
option.
-Meridian drawing algorithm adjusted to (hopefully) always draw the lines 
of equal longitude to the bottom or top of the map in orthographic mode.
-Added a test for field overflow in the first derivative of mean motion 
(dx/dt, the parameter following the epoch on Line 1). Field overflow is 
indicated by a numeric field of ".********" and it is now set to a value of 
1 or -1 depending upon the leading sign. This is often an indication that 
the satellite has decayed or soon will decay.
-Corrected the default directory upon return from DOS using F9 on the Main 
Menu. (Default directory was left where the user last logged and file 
STSPLUS.INI was written there instead of where it belonged.)
-Corrected file list to show CIS.TRK instead of USSR.TRK and updated the 
distribution files accordingly.
-Description of TDRS satellite locations in the text corrected.
-Description of MCX, MCP, and XYZ map database files corrected to restore a 
line of text that was dropped by my word processor.

Version 9241 was released for beta testing only.


Version 9240 -- October, 1992
-----------------------------

                           *********************
                           *  IMPORTANT NOTES  *
                           *********************

     After almost four years, I have at last discontinued support 
     for the simple orbital model in STSORBIT PLUS. Users who wish 
     to continue using the simple orbital model must use prior 
     versions of STSPLUS or use the original STSORBIT program. I 
     plan to add manual generation of estimated 2-line orbital 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 140


     elements for the Space Shuttle in the next release of STSPLUS.

     Motion maps are available only with rectangular projection.

     The FAST modes are still not really repaired. Maybe I'll get 
     around to that in the next release ...

     The South Atlantic Anomaly (SAA) is disabled for 
     orthographic modes until I digitize a better model from 
     NASA's Mission Charts.

-Version 9240 is a MAJOR UPGRADE and is the initial public release with the 
orthographic projection techniques used in my program ORTHOGRAPHIC EARTH 
VIEW.
-While the principal new feature is the orthographic projection, that 
addition affected almost all parts of the program and many different 
routines have been updated or modified. I have also rewritten the AOS/LOS 
code for TDRS and the user's location. Although considerable beta testing 
has been performed, there are surely a few bugs that have not yet been 
discovered. Special thanks to Joel Runes for his help with the beta 
versions! Comments and bug reports are welcome.
-Added Orthographic Projection maps and new map databases. Orthographic 
maps are selected using the letter "O" when the map is displayed or by 
selecting "ORTHO" using F10+F6 from the Main Menu. PgUp, PgDn, Home, and 
End may be used to select the magnification factor. See the text for a full 
description.
-A math coprocessor is REQUIRED for the orthographic maps. Orthographic 
maps require MUCH more computation time. Most computers not equipped with a 
math coprocessor chip, even 386 systems, will yield poor or unacceptable 
performance in orthographic modes. Typical orthographic map drawing times 
range from 5 or 10 seconds for a 486DX/33 to 600 seconds or more for an 
8088 without a math coprocessor!
-All rectangular projection map routines have been rewritten to use the new 
indexed map database files and the maximum zoom factor has been increased 
to a field of view of 30 degrees. This yields much improved map detail at 
higher zoom factors and decreases the map drawing time in most cases. The 
old map database file, STSPLUS.MVF, may be deleted.
-Because of their size, the high detail map database files cannot be 
downloaded from the RPV ASTRONOMY BBS except for callers with 9600 or 
faster baud modems. See file README for additional information on these 
files.
-The TDRS sub-satellite coordinates are now included in STSPLUS.INI and may 
be updated by displaying the appropriate satellite. For TDRS East display 
NORAD #19883, and for TDRS West display NORAD# 21639. See the section "TDRS 
Satellite Features" for additional information. Thanks to Jim Henderson of 
NASA White Sands (and others) for the suggestion.
-Changed TDRS coverage algorithm to reflect actual coverage as a function 
of satellite altitude above the Earth's surface. Provided current TDRS 
position data is used, accuracy should now be on the order of tens of 
seconds. Prior versions assumed a "customer" satellite orbital altitude of 
approximately 160 miles.
-Added location and features labels to all maps, enabled or disabled by 
F10+F3+F9 from the Main Menu. Labels are contained in file STSPLUS.LOC. See 
the section "Location and Features Labels" for additional information.
-Rewrote the time base algorithms to better accomodate slower computers and 

Program STSORBIT PLUS Satellite Orbit Simulation                   Page 141


the longer calculation times required in orthographic modes. The program 
now operates correctly even when the map drawing and updating times are 
longer than ten seconds. Updating of the spacecraft circle of visibility, 
for example, will occur at ten second intervals if the necessary 
calculations and screen operations can be performed in less than one 
second; if not, the update interval will be adjusted as necessary.
-Partly because of the new timebase algorithms, the ground track has been 
changed. The "minute marker" dots are now yellow when DOTS+LINES are 
enabled and the dots no longer change color. (A synchronization problem.)
-Changed the algorithm for the Circle of Visibility to correctly calculate 
near the poles. The new algorithm is now used in all map projections. Users 
who complained about the circles of visibility for high inclination orbits 
will find them now correct -- although somewhat slower. The algorithm was 
adapted from FORTRAN code generously supplied by Paul Traufler. Thanks 
yet again, Paul!
-Changed most circle of visibility plotting routines from double to single 
precision and used in-line code to improve performance.
-Added a black dot on the satellite icons to show the center of the icon.
-Corrected a fatal error if the map data files were missing. This problem 
was frequently caused by using an old version of PKUNZIP (earlier than 
Version 1.10) which could not unpack the map data file, the only file which 
used the most recent compression algorithm. No error message was displayed 
and the computer had to be rebooted. (Users who downloaded the program from 
NASA SpaceLink BBS often had this problem since NASA had the wrong version 
of PKUNZIP posted -- which they corrected at my request!)
-Corrected an error in the internal tracking station data which caused a 
fatal Basic PDS Error 3 ("Syntax Error") if file STSPLUS.TRK was missing.
-Changed "current file" display to use inverse video when selecting 2-line 
elements files. The color change used in prior versions did not show on 
monochrome systems!
-Corrected a bug in the 2-line file selection logic that prevented entry of 
a specific filename and improved the error trapping.
-Corrected the longitude of Cape Canaveral in STSPLUS.CTY so that it was 
not out in the Atlantic Ocean. (Thanks to all of you who reported it!)
-Increased internal STACK size to 6144 bytes (vs. 3072) in the hope of 
eliminating some reported memory problems (which I can't duplicate).
-Corrected a minor bug in the (25 line modes only) large character display 
of MET/T+Epoch if the days were four characters; the time was shifted left 
one digit. Days may now range from -999 to +9999. Also eliminated a double 
minus sign if MET or T+Epoch was negative.
-Corrected a minor bug in satellite coordinates if a distance was greater 
than -99999.99 km/nm. The display wrapped because of field overflow. The 
distance is now shown as -NNNNNN.N (one less digit to the right of the 
decimal point) for large distances. Most folks won't notice this one!
-Corrected a minor bug in large character negative MET/T+Epoch that caused 
the time to be green for one second before turning red under certain 
circumstances.
-Corrected an occasional bug which caused the colors to go awry or to 
monochrome.
-Various minor cosmetic bugs.


(Intermediate update notes deleted to save space, available on request.)



Program STSORBIT PLUS Satellite Orbit Simulation                   Page 142


Beta Version 9137 -- September, 1991
------------------------------------
-Initial public beta version.