FX - TW-523 Special Effects Interpreter - Version 1.00
Copyright 1992-93 by Bruce Christensen. All Rights Reserved.


==============================================================================
Introduction:
==============================================================================

FX.EXE is a DOS-based X10 command interpreter for the TW-523.  Valid
X10 commands are ON, OFF, DIM and BRIGHT. These commands can be input
from the DOS command line, or they may be read from a "script" file.

If you are familiar with XA (X10 Command Interpreter for the CP-290),
then you should grasp the concepts of FX very easily. If you are not
familiar with XA, and you own CP-290, then you should download XA to
expand the capabilities of your CP-290.

A special feature of FX is its ability to send SIMULTANEOUS Bright
and Dim commands to multiple X10 modules. This allows you to create
some very interesting lighting effects.  My primary use for this
program is for Halloween and Christmas lighting. 

FX communicates with the TW-523 via your computers parallel port
(LPT1...LPT3).  See the section "LPT Wiring" for the I/O lines FX
uses to communicate with the TW-523.

This document is filled with many examples. Most examples use the
command line to issue commands. Complete commands from the DOS
command line must be enclosed in "quotation marks":

        FX "A1 ON"


However, when commands are read from a script file, they are not
enclosed in quotation marks:

        A1 ON


==============================================================================
Christmas Lighting:
==============================================================================

Our indoor Christmas tree, as well as several outdoor trees are
decorated with multiple strings of solid color mini-lights: RED,
BLUE, GREEN, WHITE.  Each color is controlled by a Lamp/Dimmer module
with a unique house code:

        Lamp/Dimmer controlling RED   : L1
                                GREEN : M1
                                BLUE  : N1
                                WHITE : O1

The intensity of each string may be continuously varied so that the
trees are always changing colors. The really slick effect is when you
DIM one color and BRIGHTEN another color at the same time. Your tree
will change from Red to Blue (or whatever you program) in about a
second.

I've included a command file (XMAS_FX.CMD) to demonstrate how I
program these effects. The rest of this document explains the command
line arguments and language syntax of FX.


==============================================================================
FX Syntax and Arguments:
==============================================================================

FX Syntax:
--------------------------------------
FX is invoked by typing FX along with any of the following arguments.
These arguments are optional. The default value will be used for non-
specified arguments.


        FX [f=script_file] [L=1...3] [o=xxx] [-e] [+h] ["command"...]


Arguments:
--------------------------------------
[f=script_file]

        This is the name of a file containing commands that are read 
        by FX and sent to the TW-523. To have FX read the example 
        XMAS_FX.CMD script file:

                FX f=XMAS_FX.CMD


        If no "commands" are present on the command line, and no script file
        is specified, then FX will attempt to read the file FX.CMD (default).


[L=1..3]
        Specifies the LPT port that the TW-523 is connected to. There are
        three possible LPT ports supported in standard PC configurations.

                LPT     I/O addr
                ===     ========
                 1       0x378
                 2       0x278
                 3       0x3BC


        On some machines (including combination monochrome display adapters
        and printer cards), LPT1 uses I/O port 0x3BC. 

        The default port is 1 if this option is not specified.


[o=xxx] 
        Specifies a special I/O port address. Use this parameter if your
        LPT I/O address is something other than one of the values located
        in the above table. The default address is 0x378.


-e
        This option will prevent FX from sending any commands to the TW-523.


-h
+h      
        Displays a "usage" screen listing available commands, syntax, and
        the FX version level.


["commands..."]
        FX will execute commands from the DOS prompt, or from within 
        batch files. Commands must be enclosed in "quotation marks"
        when the are executed in this manner. 

                FX "A1 OFF" "B1 OFF" "C1 OFF"



==============================================================================
FX Tokens
==============================================================================

This section describes each of the tokens that FX understands.  Most
commands are composed of multiple tokens. In certain cases, the order
of the tokens is not important. For example, the command:

        FX "A1 ON"     may also be written as:
        FX "ON A1"    


In other instances, the tokens must be arranged in groups. Their order is
important. For example, the command to dim a module is "DIM #levels".
You would therefore program the command as:

        FX "A1 DIM 20" 
        FX "DIM A1 20" <--- This is illegal.


Therefore, token groups dependent on order will be enclosed in curly 
braces { }. 


{DEFINE X Y}
--------------------------------------
This token grouping allows you to substitute a text string (X) for another
text string (Y). For example, to assign a module (addressed as L1) a name
such as RED, you would define it as follows:

        DEFINE RED L1
               (X) (Y)


Now, instead of issuing a command such as:

        FX "L1 ON"    you can use a more natural command:
        FX "RED ON"


A SPACE character separates the X from the Y string. The Y string can have
multiple spaces. If you want to use multi-word strings for X, use the 
UNDERSCORE character:

        DEFINE LOW DIM 0
                X  <-Y->

        DEFINE XMAS_TREE E2
               <---X--->  Y


The DEFINES used in the XMAS.CMD file are listed below. These DEFINES will
be used in examples throughout this document.

        DEFINE RED    L1
        DEFINE GREEN  M1
        DEFINE BLUE   N1
        DEFINE WHITE  O1
        DEFINE PC     C4
        DEFINE PORCH  A9


ON
--------------------------------------
Turns ON the specified module.
        
        FX "A1 ON"


OFF
--------------------------------------
Turns OFF the specified module.
        
        FX "B1 OFF"


{DIM #levels}
--------------------------------------
DIMs the specified module by # levels. There are approximately 18
levels of brightness supported by X10 wall switch/lamp dimmer modules.
The '#levels' tells FX how many times to send the DIM command to the
module. The minimum value must be 1, the maximum value can be any positive
number greater than 1.

To dim module C2 by 10 levels from its current level:
        
        FX "C2 DIM 10"

Over time, a module may not be at its expected brightness level when 
multiple DIM (or BRIGHT) commands have been sent to it. This may be
caused by lost or garbled transmissions from the TW-523. To offset
this possibility, when dimming a module to its completely dimmed
state, set the number of levels to a higher than normal number to
ensure the module is completely dimmed:

        FX "D4 DIM 25"


{BRIGHT #levels}
--------------------------------------
BRIGHTens the specified module by # levels. There are approximately 18
levels of brightness supported by X10 wall switch/lamp dimmer modules.
The '#levels' tells FX how many times to send the BRIGHT command to the
module. The minimum value must be 1, the maximum value can be any positive
number greater than 1.

To brighten module A5 by 6 levels from its current level:
        
        FX "A5 BRIGHT 6"


Over time, a module may not be at its expected brightness level when 
multiple BRIGHT (or DIM) commands have been sent to it. This may be
caused by lost or garbled transmissions from the TW-523. To offset
this possibility, when brightening a module to its completely bright
state, set the number of levels to a higher than normal number to
ensure the module is completely brightened:

        FX "A1 BRIGHT 25"


Additional BRIGHT / DIM Examples
--------------------------------------
Assuming the RED lights (module L1) are fully on (100% brightness), to dim
them by 25%:

        RED DIM 5


If BLUE is completely DIM (0% brightness), to brighten them to 50%;

        BLUE BRIGHT 10


If GREEN is fully bright and you want them completely dimmed:

        GREEN DIM 20



Simultaneous Bright/Dim Commands
--------------------------------------
Simultaneous commands may only occur with the BRIGHT and DIM tokens.
In addition, the modules controlled simultaneously are required to
have unique housecodes. For example, you could control A1, B1, C1,
D1...P1 simultaneously in one command. You CAN NOT control A1, A2, A3
simultaneously in on command.

You must use the "+" (plus) symbol between multiple commands to tell
the FX interpreter that these commands are to be treated as
simultaneous. Once a module is commanded to brighten or dim, it
continues that command no matter what subsequent modules are issued
for the rest of the command.

        BLUE BRIGHT 1 + GREEN DIM 20


In the above example, BLUE is issued a command to brighten by 1
level.  Immediately following the bright command, GREEN is dimmed by
20 levels, however BLUE continues to brighten for the duration of the
entire command.  Therefore BLUE receives a total of 21 BRIGHT
commands, GREEN receives 20 DIM commands.

You can delay the effects of simultaneous transmissions by altering
the "levels" of each command. Assuming all lights are fully on, the
following command will start fading WHITE 5 levels, then begin fading
RED 5 levels (WHITE continues fading), then GREEN, then BLUE. Note
that BLUE uses 20 levels to reach its desired state - the other
modules recieve more commands than actually needed to get to the
desired state.

        WHITE DIM 5 + RED DIM 5 + GREEN DIM 5 + BLUE DIM 20


A module is NOT allowed to receive different commands on the same line:

        RED DIM 5 + BLUE BRIGHT 5 + RED BRIGHT 10 

See the file XMAS_FX.CMD for more examples of simultaneous programming.


{DELAY seconds}
--------------------------------------
DELAY allows you to wait "seconds" before continuing on with the rest
of the program. To wait 5 seconds between commands:

        RED BRIGHT 1 + WHITE BRIGHT 1 + GREEN DIM 1 + BLUE DIM 20
        DELAY 5
        WHITE DIM 20


Support for program looping
--------------------------------------
You may repeat a series of commands as often as you like by using the
"GOTO label" and ":label" tokens. The ":label" token identifies a
location in the file that FX may reference with a GOTO command later
on. The label must have been parsed prior to the GOTO token. 

The GOTO command will jump to a previously defined label. You may
specify the number of times the jump is to be performed. To repeat a
sequence of instructions 5 times:

        :HERE
        RED DIM 1 + BLUE BRIGHT 20
        BLUE DIM 1 + RED BRIGHT 20
        GOTO HERE 5


Following the 5th pass of the GOTO statement, FX continues with the
remaining commands in the command file.

If you do not specify a repeat value, FX will continue to execute the
GOTO statement inedefinately:

        :REPEAT
        RED DIM 1 + BLUE BRIGHT 20
        BLUE DIM 1 + RED BRIGHT 20
        GOTO REPEAT


The :EXIT label has special meaning to the FX interpreter. FX will
always search for :EXIT whenever the <ESC> key has been detected.
This allows you to create a controlled shutdown command sequence
ensuring certain modules are in a desired state.

        :EXIT
        RED OFF
        GREEN OFF
        BLUE OFF
        WHITE OFF
        PORCH BRIGHT 20
        PC OFF


If :EXIT is not present, FX will simply stop what it is doing and
return to DOS. 


{TIME hh:mm [AM PM]}   
Controlled Shutdown Time
--------------------------------------
The PC I use to control the lighting sequences is activated at Dusk by
the CP-290. Once this PC is booted it begins transmitting X10
commands via the TW-523 module. This PC saturates the powerline with
continuous X10 commands leaving virtually no bandwith for the CP-290
or other transmitters to transmit clean X10 commands to shut the PC
down later on. 

Using TIME hh:mm at the beginning of the script file will ensure that
FX stops executing at a specified time:

        TIME 11:30 PM


After every X10 command is issued, the FX interpreter will compare the 
current time with the preset time. When the times match, the shutdown
portion of the script file is executed if the :EXIT token is located.
If :EXIT is not included, then FX simply stops and returns to DOS.


==============================================================================
LPT Wiring
==============================================================================

The TW-523 was developed to allow vendors to interface their
equipment with X10's patented communication protocol. It was not
intended to be sold to consumers, therefore there is no "standard"
configuration for attaching the TW-523 to your computer. There are
various kits that offer serial and parallel port connectors, but
these kits may differ from vendor to vendor. 

The software used in FX is only capable of handling LPT communications
with a 25 pin connector using the following pinout diagram. This pinout
is compatible with the TW-523 kit sold by HCC (although that is subject 
to change).

    PC's LPT port                                         TW-523 RJ
         (25 Pin)                                         connector
    =================                                    =============
        Pin   2 -+
                 |
              4 -+     
                 |
              6 -+
                 |     (Pins 2,4,6,8 are tied together)
              8 -+------->>-------(Transmit)------>>---------- 4


             10 -+
                 |     (Pins 10 and 14 are tied together)
             14 -+-------<<-------(Receive)-------<<---------- 3
                        (These lines not currently used)


             25 -------------------(Ground)------------------- 2


             17 ---------<<---------(60hz)--------<<---------- 1

Radio Shack sells a 25-pin Male D-shell kit with a 6-pin RJ connector
that allows you to create the LPT pinouts as described above.


A final note on parallel ports - some manufacturers of I/O cards with
LPT ports do not support all the I/O data lines as specified by
IBM. This is most noticable on some very early I/O cards. If you
experience problems such as "No AC sync signal detected", try a
different LPT port.


==============================================================================
Other X10 Programs by Bruce Christensen 
==============================================================================

XA - X10 Command Interpreter
--------------------------------------

XA translates English-like sentences into commands or events that are
understood by the CP-290. XA receives its input directly from the DOS
prompt (XA "A1 ON") or it can read an entire script from a file (XA
F=XA.CMD).

XA can maintain your CP-290's event schedule automatically. XA comes
with a utility that allows new events to be downloaded on a weekly
basis without any interaction from a user.  XA calculates SUNRISE and
SUNSET times based on your latitude and longitude, and automatically
compensates for any Daylight Savings changes. XA can be programmed to
handle specific dates that may be weeks, months, or years in the
future.  Events may also be excluded on certain dates.

XA also supports a power-fail recovery mode which restores all
programmed modules to their expected state. XA supports the CP-290
"undocumented" commands ALL_LIGHTS_ON and ALL_UNITS_OFF. XA allows
you to append new events to your existing CP-290 schedule easily from
the DOS command line. XA can synchronize either your PC or CP-290
internal clocks to an accuracy of 1 second. XA can monitor (display)
events as the CP-290 executes them, it can also log these events to a
file. 

XA is the most powerful shareware program available for the CP-290.
You will never need to use the original X10-supplied software again.
When you register your copy, you also get enhanced programming
capabilities such as IF/ELSE constructs, Logical/Arithmetic/Boolean
operators, user variables, and the ability to interface with I/O such
as the joystick port. 

The current version of XA is 2.00. It has been uploaded to numerous
BBS's, including: CompuServe, America OnLine, PC-Ohio, HAL, Baran-
Harper, Circuit Cellar.  Look for the file: X10XA200.ZIP.


XT - X10 TSR
--------------------------------------

XT is a Terminate-Stay-Resident program that sits silently in the
background waiting for you to activate it with the proper keystroke.
This means you can instantly call it from within any text-based
application. When activated, it displays a list of all modules that
you can control with the CP-290. Each line on the list contains a
description of the module, its address, and its current status.  You
select the module you want to control, and then choose the action
(ON, OFF,DIM).

Since XT is resident, it continuously monitors the serial port for any
communication transmitted by the CP-290 (such as when an event is
issued or when one of the buttons on the unit is pressed). The status
of the each module will always be reflected in the pop-up menu.

The current version of XT is 1.00. It has been uploaded to numerous
BBS's, including: CompuServe, America OnLine, PC-Ohio, HAL, Baran-
Harper, Circuit Cellar.  Look for the file: X10_TSR.ZIP.

A newer version is planned for release during January 1994. This
version of XT, (1.02) will come with a utility called XTS.EXE. XTS
has direct access to XT's database of module states. Every command
issued by the CP-290 is captured and stored by XT. XTS can return the
module states (via DOS 'errorlevel' statements) allowing you to write
batch files that react to a modules X10 status. 
Look for file: X10XT102.ZIP.




==============================================================================
Registration
==============================================================================

FX is a copyrighted program. Please support shareware and register this
software. Requested fee is $10.00 - US funds.
Please describe how you received the program and what your primary
use is. Also include any comments or suggestions for new releases.
When distributing this program to other users, please leave all the 
original files intact.


Author Information:
--------------------------------------
Bruce Christensen
6594 Hudson Ave.
Mentor, OH.  44060-4545  USA

CompuServe     : 73201,1531
America On-Line: AuggieBen
Prodigy        : MHNC93A