"BEAM" - QUICK, SIMPLE BEAM ANALYSIS: EVERYTHING IS BUILT-IN !   12/93


   BEAM.EXE = Executable Quick Basic Program that analyses 10 different
              load conditions, 6 different materials (Pine, Oak, Steel,
              Stainless, Aluminum, Brass, Concrete, and User-Defined).
              Predefined cross sectional shapes of Angle, I-Beam, Pipe,               
              Rectangular Tube, Solid and T-Beam (same as Angle).


   Sample Problem 1: 150 Lb man standing on 8 foot long 2x4.
   ---------------------------------------------------------
   RUN: Shape ?       B  (A 2x4 is a 'bar' of wood)
        Span ?       96  (Inches, Ends of 2x4 nailed to boards)
        Height ?     3.5
        Width ?      1.5
        Material ?    6  (Pine)
        Condition ?   1  (Center load, ends basically free to rotate)
        Load ?       150
        Add Inertia ? 0  (No added strength from floor or other boards)

        Stress     = 1170 Psi    Stress Limit = 1400 Psi  ; Beam will 
        Deflection = .30 Inch    Defl. Limit  = .53 Inch    not break...    
        
------------------------------------------------------------------------------
   
   Sample Problem 2: 16 1/2 Foot Garage Door Beam
   ----------------------------------------------
   
   Info: House is 28 feet wide. 24 Inch Snow = 2.4 Inch Water
                                Water Weighs 5 Lb/Inch Depth
         
         Total Load on Roof: Truss Weight ......... 2.2 Lb/Ft2 
                             Insulation (12 Inches) 1.2
            |--- 14'--|      Ceiling .............. 1.5
            /\               1/2" Roof Sheeting ... 1.1 
          /    \             Shingles, 2 Layers ... 5.2
        /        \           Snow (24 Inches deep) 12.0 
      /            x         --------------------------
      |            | Garage        Roof Pressure = 23.2 Ib/Ft2
      |____________| Beam          (23.2/144 = .16 Psi)


     RUN:   Shape ?      B  (bar)
     ---    Name ?       2 x 12 - Three of Them
            Span ?       198  (inches)
            Material ?   6  (pine)
            Height ?     11.5  (actual height of 12" beam)
            Width ?      4.5   (Three 2 x 12's, 1.5" wide each) 
            Inertia ?    0     (no help from roof sheeting)
            Condition ?  3     (evenly distributed load)
            Pressure ?   .16   (Psi)
            Load Width ? 168   (14 feet wide roof x 12 In/Ft) 
                               (width of the load)  
                               
      Answer:  Stress = 1333 Psi      Stress Limit = 1400 Psi ... Good !
               Deflection = .5 Inch   Defl Limit = (1/180 x L)
                                              or 1.10 Inch
                                                     
-----------------------------------------------------------------------------


    Sample Problem 3: Beam under Floor of 3' x 8' Steel Water Tank
    ---------------------------------------------------------------

    Hint: Angle iron welded underneath the tank in the "L" position
    ----  effectively gives a channel section and is very strong...
                           ||
                           ||                     
     Closeup of Floor ---> ==========================================
                                                   ||        
                 ____________                      ||        
                /|          /                      ||_______ 
              /  |_______ / | 5' Deep               -------- Angle
            /___________/   |                             ( L2x2-1/4 )
            |           |  /
            |___________|/  3' Wide
                  L     
            <---8'------>
                                                            3            2
       If the Tank is filled it will have 5 Ft x 62.4 Lb/Ft or 312 Lb/Ft
       of pressure on the floor. 312/144 In2 = 2.166 Psi Floor Pressure.

       The beam could be expected to support 1/2 the total floor pressure:
              
              |   wt beam supports     | outer wall supports 1/2 of floor
              |      <--------->       |
       Floor: ==========================
               <---4'---> |_ <---4'--->

       RUN:  Shape ?     C     (angle welded to flat plate = channel)
             Span ?     36     (width of tank in Inches)
             Height ?    2.25  (Ht of angle plus 1/4 floor plate)
             Width ?     2     (width of angle iron)
             Thick ?    .25
             Material ?  1     (Steel)
             Condition ? 3     (Uniformly loaded with free ends)
             Pressure ?  2.166 (Psi on the tank floor)
             Press Width ? 48    (width of supported area)


        Stress = 17000 Psi    Stress Limit     = 18000 Psi... Good design!
        Defl   = .068 Inch    Deflection Limit = .20 Inches