NET-TIME 
                              Version 2.00a 

                   Copyright (C), 1993, 1994, G.W. Mays
                                

                            3314 Prince George
                        San Antonio, Texas  78230


      
                            WHAT IS NET-TIME?

     NET-TIME is a package of programs which allow systems on your network
to remain synchronized with respect to date and time.  One system is used
to continuously broadcast the date and time.  Other systems may then
receive these broadcasts.  The programs which provide this service are
DOS TSR's, typically less than 2K bytes in size.  There is support for
NetBIOS based networks as well as Novell Netware.


                            SHAREWARE NOTICE

     NET-TIME is a "Shareware" product.  It is the copyrighted work of G.W.
Mays.  It is not free; nor is it in the public domain.  All rights to this
product are retained by its author.

     You are free to try NET-TIME for 30 days in order to ascertain whether 
or not its functions are valuable to you and whether or not it performs to 
your satisfaction.  After 30 days, you are expected to either register and
pay for NET-TIME, or, discontinue your use of NET-TIME.  Shareware authors
trust in your integrity.  Please don't let us down.  

     You are encouraged to further disseminate NET-TIME to other interested
parties.  However, you must pass along the complete product.  Please do not
break the package into pieces.  You may not sell this program to others.
However, organizations that specialize in the distribution of shareware are
allowed to charge a small fee for their efforts provided that the product
fully retains its identity and integrity, and that their customers are made
to understand the shareware nature of the contents.

     
                               REGISTRATION

     Register your use of NET-TIME by printing out a copy of the ORDER.TXT
file provided with the package (COPY ORDER.TXT PRN).  Fill it out, make your
check payable to G.W. Mays.  Mail it to the address which appears at the top
of the form.

     In return, you will receive a copy of the most recent version of the
NET-TIME software and evaluation copies of RightTime (from Air Systems
Technologies) and TimeSet (from Life Sciences Software).  In addition, your
name will be added to our mailing list so that you may be informed of any
noteworthy changes and additions to NET-TIME.  Favorable upgrade pricing for 
future versions of NET-TIME will be afforded to registered users.  Your
registration also entitles you to technical support.

     
                                DISCLAIMER

     No software product is infalible.  NET-TIME is no exception.  Hence,
we will not be responsible for damages that might result, either directly or 
indirectly, from the use of NET-TIME.  We assume no responsibility for 
consequential damages arising from the use of our product.  In addition, we
disclaim, to the largest extent possible, any warranties of merchantability
or suitability for a particular purpose.


                               INSTALLATION

     NET-TIME is generally installed in its own subdirectory on your hard
disk.  Create a suitably named subdirectory to contain NET-TIME.  Copy the 
"NETIMxxx.ZIP" file to that subdirectory.  Place youreself in that subdir-
ectory, and "unzip" it.  The components of the NET-TIME product should
"explode".  
                
        Example:
                C:
                MD \NETTIME
                COPY A:\NETIMxxx.EXE C:\NETTIME
                CD \NETTIME
                NETIMxxx

    Examine the READ.ME file.  It contains information pertinent to your 
use of NET-TIME.  Changes to the documentation that are "late breaking" in 
nature, appear here.



                                HOW TO USE

     Usually, NET-TIME is implemented with a single system on your network
that is considered to be the "MASTER TIME STANDARD".  That system should
use the appropriate NET-TIME program to broadcast the date and time to the
rest of your network.  Other systems on your network which require coordin-
ated date and time, should use the appropriate NET-TIME program to keep the
system clock synchronized with the broadcaster.  

     The NET-TIME program which is appropriate for your use depends upon
the network operating system you employ.  If your network is Novell, you 
will probably want to use the IPX versions of the NET-TIME programs.  If
your network is NetBIOS-based, then the NETBIOS versions of the the NET-TIME
programs are in order.

        Programs:
                TIMESNDN        Broadcast time via NetBIOS
                TIMERCVN        Receive NetBIOS time broadcasts
                TIMESNDI        Broadcast time via IPX
                TIMERCVI        Receive IPX time broadcasts

     The NET-TIME programs are TSR's.  Program sizes are various, but are
typically less than 2K bytes when resident.  All may be loaded high if your
system supports the capability.  Remember that NET-TIME requires the 
services provided by some of your network software; so be sure to load
IPX (for Novell) or NetBIOS before NET-TIME.


                               CONFIGURATION

     NET-TIME comes with a configuration utility named TIMECFG.  Place 
yourself in the directory into which you installed NET-TIME and execute
TIMECFG.  Alter configuration values to suit your needs.  Note that the
default values will probably work in most circumstances.  NET-TIME system
parameters that are under your control are...

     NETBIOS NAME OF BROADCASTER.  This is the NetBIOS name of the
        broadcast program.  It may be 1 to 16 characters in length and
        should not contain embedded blanks.  See the "gory" details
        of your NetBIOS to determine any restrictions that may apply.
        The default is "TIMESERVER".

     NETBIOS NAME OF RECEIVERS.  This is the NetBIOS name of the programs
        which receive the broadcasts.  The default is "TIMECLIENT".  See 
        the notes above.

     BROADCAST INTERVAL.  This is the time interval between Date/Time
        broadcasts expressed in "ticks".  There are 18.2 ticks per 
        second.  The default is 91 which translates to 5 seconds.

     IPX SOCKET.  This is the IPX socket number expressed in hexadecimal.
        DO NOT BYTE-REVERSE THIS VALUE.  Simply enter the socket number
        you wish to use; NET-TIME will perform the translation to non-Intel
        format as needed by IPX.  (Sockets serve to identify the process
        which is using IPX services).  The default is (hex) 4949.

     LAN ADAPTER NUMBER.  This is the NetBIOS LAN Adapter Number.  If
        you have a single network adapter, then this is generally set to
        zero.  The default is 0.

     INITIAL WAIT TIME.  In 2.00a, this parameter applies only to the
        the TIMERCVN program.  It specifies the amount of time, in
        "ticks", that TIMERCVN will wait for a time broadcast during
        program initialization.  Typically, this should be set to the
        same value as the BROADCAST INTERVAL.  See "Notes on Program
        Initialization" in the section below.

     TIMECFG modifies the .COM files directly.  By default, TIMECFG
     will look for the NET-TIME programs in the current directory. 
     If the environment variable "NETTIME" is defined, it is assumed
     to specify the path to the NET-TIME programs.


                         USE WITH OTHER PROGRAMS

     Providing a single source for network date and time is a
double-edged sword.  While it serves to provide uniformity and is
relatively fault-tolerent, this source will also proliferate bad
information to all of its clients if it comes from a tainted or
questionable origin.  

     We suggest that you employ the services of RightTime, from Air
System Technoligies of Dallas, Texas, and TimeSet, from Life Sciences
Software of Stanwood, Washington.  Both are valuable products in
their own right.  Working together, and in conjunction with NET-TIME,
you can expect a highly accurate and reliable network time source.  

     RightTime is a software product which adaptively regulates the
accuracy of the clock within the PC you use to broadcast the date and
time.  Without RightTime, PC's tend to "drift" slightly each day with
respect to their timekeeping.

     TimeSet is a software product which automates access to dial-up
time sources such as NIST in Boulder, Colorado, and the U.S. Naval
Observatory in Washington, D.C.  This simplifies the process of
obtaining and setting accurate time on your PC.

     Both products are available on better bulletin boards
everywhere.  If you have difficulty locating either of them from your
usual sources, try the Air System Technologies BBS at (213) 869-2780.
     
                        
                           CONFIGURING A BRIDGE

     The NetBIOS version of NET-TIME may be used to form a "time 
bridge".  Given a system with two (or more) LAN adapters connected
to different networks, you may execute TIMERCVN to receive the
date/time broadcasts from a specific adapter (and thereby from a
specific network).  You may then execute TIMESNDN (or several copies
of same) to rebroadcast date/time on other adapters.

     IBM's NetBIOS (NETBEUI or TOKRUEI) supports only two LAN adapters
numbered 0 and 1.  Hence, only a trivial bridge is possible under these
circumstances; receiving broadcasts on one of the adapters and 
rebroadcasting same on the other.

     Performance Technology's NetBIOS is not constrained to two
LAN adapters.  In fact, the author has configured a bridge in the PT
PowerLan environment with five adapters.  In this case, one copy of
TIMERCVN receives date/time from adapter 0; four copies of TIMESNDN
execute concurrently to rebroadcast date/time via the other four
LAN adapters.


                           COMMAND LINE OPTIONS

     Various parameters may be specified on the command line when the
NET-TIME programs are executed.  The allowable options depend upon the
program in question.  Note that the parameters under your contol via 
the command line are the same as those that are manipulable by way of
the TIMECFG program.  Specifically...


     TIMESNDI -- Broadcast time via IPX

          /S=hexsocket        IPX socket.  A 4 digit hexadecimal 
                              value.  DO NOT BYTE-REVERSE.
                              Default:  4949 hex.
          /I=interval         Broadcast interval in "ticks".  A 1 to
                              4 digit decimal value.  There are 18.2
                              ticks per second.  Default:  91.

     TIMERCVI -- Receive IPX time broadcasts

          /S=hexsocket        IPX socket.  A 4 digit hexadecimal 
                              value.  DO NOT BYTE-REVERSE.
                              Default:  4949 hex.
     
     TIMESNDN -- Broadcast time via NetBIOS

          /I=interval         Broadcast interval in "ticks".  A 1 to
                              4 digit decimal value.  There are 18.2
                              ticks per second.  Default:  91.
          /A=adapter#         LAN adapter number.  A 1 digit decimal 
                              value (0 to 9).  Default:  0.
          /F=send_nbname      NetBIOS name from which the broadcasts
                              are sent.  Default:  TIMESERVER.
          /T=recv_nbname      NetBIOS name to which the broadcasts are
                              sent.  Default:  TIMECLIENT.

     TIMERCVN -- Receive NetBIOS time broadcasts

          /A=adapter#         LAN adapter number.  A 1 digit decimal 
                              value (0 to 9).  Default:  0.
          /N=recv_nbname      NetBIOS name to which the broadcasts are
                              sent.  Default:  TIMECLIENT.
          /I=init_wait        Wait time in ticks for initial broadcast.

     The option letters (A, I, F, etc.) are case insensitive.  Also,
the use of the equal sign (=) is optional.  In addition to the options
specific to the individual programs, each program responds to the
following:

     ALL PROGRAMS

          /H or /?            Help.  Displays a brief description of
                              the options the program recognizes.

          /U                  Unload.  Don't get excited.  It's not
                              implemented yet.  I had to leave
                              something for the next release.

          
                     NOTES ON PROGRAM INITIALIZATION

     The program initialization logic of TIMERCVN version 2.00a has
been enhanced.  Behavior of the program at initialization largely
depends upon the setting of the INITIAL WAIT TIME parameter, which
may be set via TIMECFG or by way of the command line (/I=...).  If
INITWAIT is set to zero, TIMERCVN does not attempt to capture a 
date/time broadcast while it is initializing; it simply prepares to
receive such a broadcast and remains resident.  If INITWAIT is 
non-zero, TIMERCVN will delay for the period specified in an attempt
to capture a date/time broadcast.  During this delay, four outcomes
are possible:  (1) a broadcast is received, (2) the ESC key is struck,
(3) another key is struck, or (4) no broadcast is received within the
INITWAIT interval.  In the first instance, TIMERCVN's behavior is 
rather obvious, it displays the date and time and proceeds to terminate
and stay resident.  If the ESC key is struck, TIMERCVN will cease its
attempts to capture a date/time broadcast, and, it will terminate
WITHOUT remaining resident.  Entering a key other than ESC, will result
in cessation of attempts to capture a date/time broadcast, but TIMERCVN
will remain resident.  If however, attempts to capture a date/time
broadcast "time out", TIMERCVN will simply display the "No broadcaster
detected" message and remain resident.


                          CONTACTING THE AUTHOR

     I am always interested in improving and correcting NET-TIME.  If
you have a question or problem, or (uh-ungh) a bug, then please let me
know.  I will make every effort to make things right.  In addition, 
since the variety of network platforms upon which NET-TIME functions
is an important component of its value, I am open to adding support 
for alternative network transport mechanisms.  If you are in posession
of the pertinent programming details for a platform not currently
supported, I would appreciate the opportunity to extend NET-TIME to
meet your needs.
                                                              
     You may contact me in several ways.  I prefer to receive mail
via the Exec-PC BBS (414-789-4210) under the name "George Mays".  Also,
I check my mail every few days on Compuserve; my userid is 72300,503.

     I am considering adding a phone line and answering machine if
the need becomes clear and present.  Please understand that while I
have high hopes for NET-TIME, it does not have a significant enough
following at this point to justify a large investment in support
resources.