WinCRC

                           Cyclical Redundancy Code
                            Generator for Windows

                                 Version 1.0



































                                               Eric Roe
                                               3137 Briarcliff Avenue
                                               Vestal, New York  13850
                                               Copyright (c) 1994



                                                                      




                                                                      


        INTRODUCTION

           Welcome to WinCRC version 1.0.  WinCRC can generate many of
           the  most  popular CRCs, checksums, and message digests for
           your files. This information can be written  to  a  special
           'key file', so you can verify your files at a later time.

           "What exactly is a CRC?", you might ask.  CRCs or  Cyclical
           Redundancy  Codes are a popular method of error control for
           digital data -- like a file on your PC.   A  CRC  generator
           takes  as  input  a  stream  of  digital  data,  does  some
           mathematical footwork on the data,  and  outputs  a  number
           called  (amazingly) the CRC.  This number, which is usually
           16 or 32 bits in length, can be used to detect  any  errors
           which  might  occur  (or  be  introduced) into the original
           data.  How?  WinCRC does it by comparison.

           Say you want to verify that a certain  file  has  not  been
           corrupted.  If  you  had generated a CRC for the file at an
           earlier date, you could simply generate a CRC for the  same
           file again -- making sure you used the same CRC method.  If
           the two CRCs are identical, the file is most likely intact.
           I  say 'most likely' because there is always a possibility,
           usually extremely remote, that an error  is  not  detected.
           This method of comparing two CRCs also works with checksums
           and message digests.

           Checksums and message  digests  are  also  used  for  error
           detection.  Checksums  are  quite fast but are not terribly
           robust.  As their name implies, they are the  sum  of  each
           byte  of  the  input  data.  Since it's easy to get several
           different numbers to add to the same sum, checksums can  be
           fooled  with  very  little effort.  Message digests, at 128
           bits in length, are extremely secure. It has been theorized
           that  it  is  not  computationally possible to generate two
           files  that  will  have  the  same  message  digest.   This
           security does come at a cost -- it's more time consuming to
           generate a message digest than a CRC or checksum.

           "OK, so what good does it do me?"  A  good  question.   Any
           time  you  move  data  around  there's a chance of an error
           creeping in.  Most telecommunication software has some form
           of  built-in error detection.  That way if there's a glitch
           when you're downloading or uploading a file,  the  software
           can  re-send  the  part that got messed up.  The same thing
           can happen when you move a lot of data around on  your  PC.
           A  very  good example is a hard disk defragmenting program.
           On a large drive, hundreds of megabytes  might  be  swapped
           about.   If  a  single  bit  in  your  favorite  game  gets
           inverted...  POOF! it might not work.  Or, what happens  if
           there's  a  power  loss when defragmenting?  Which, if any,
           files might be corrupted? There's the magic of WinCRC.

           Use WinCRC to generate a key  file  for  any  files  you're
           concerned about.  Then do the defragmentation, tape backup,
           or whatever other operation you need to do to your files or


                                                                      




                                                                      


           disk.  Now when  the  defrag  program  is  done  or  you've
           restored  from  tape, use WinCRC to do a file verification.
           Any files whose CRCs have changed will be flagged and their
           name  and  error  recorded.   You  can  easily pinpoint any
           erroneous files  and  deal  with  them.   If  a  particular
           package has been zapped, you only have to re-install it and
           not worry "Maybe something else  is  messed  up  too."   It
           saves  a  lot  of  time  if you only have to re-install one
           package, rather than everything on the drive  just  to  get
           peace of mind.

           WinCRC version 1.0 can generate the following 16 bit CRCs:

                CRC-16         CRC-CCITT         SDLC
                IBM            CRC-16 Reverse    CRC-CCITT Reverse
                SLDC Reverse   IBM Reverse       LHA
                ARC            Zoo               LRCC-16

           and these 32 bit CRCs:

                CRC-32         ETHERNET          ZModem
                PK-Zip         ARJ

           It can also generate the following  checksums  (the  number
           indicates how many bits wide it is):

                Checksum 8     Checksum 16       Checksum 32

           and these 128 bit Message Digests:

                MD4            MD5 (experimental; see note)

           ** Note that many of these are actually the  same  CRC  but
           with different names.  See ALIASES for more information.


        USING WINCRC

        SELECTING A KEY FILE

           WinCRC is most useful when you are using a Key File.   When
           generating  CRCs,  WinCRC can write the filename, path, and
           CRC to the key file.  This same key file  can  be  used  to
           verify  the  files.  When  WinCRC  starts,  no  key file is
           selected and '<none>' is shown for the key file.  Press the
           'KEY  FILE'  button and the Select Key File dialog will pop
           up.  By default, files with the extension .KEY  are  shown.
           You  can  type  a  new  search  spec  and click 'OK' or hit
           <RETURN> and whatever spec you entered will become the  new
           default for this session.

           Select an existing key file or type a name in the  Filename
           edit  control.   If  the  file  exists,  it will become the
           selected key file. If not, you are prompted as  to  whether
           or not you want the file created.  Select 'YES' to have the
           file created or 'NO' to  return  to  the  Select  Key  File


                                                                      




                                                                      


           dialog.  Note that  the  file  is  NOT  created  until  you
           actually do a generate.

           Once you have selected a key file, you must check the  'Use
           Key  File'  check box to actually use the file.  The Verify
           option requires you select a key file and check the Use Key
           File option before it becomes available.

           WinCRC tests the selected key file to make sure it's valid.
           If  you're  generating  CRCs  and the key file does not yet
           exist, it is created.  If the file exists,  but  is  not  a
           WinCRC  key  file,  CRC generation or verification will not
           continue.

           Key files are standard ASCII files and  can  be  viewed  by
           most  editors  including  Windows Notepad, MS-DOS Edit, and
           DRDOS Editor.


        GENERATING

           You can Generate CRCs for files with or without a key file.
           If  you  don't  use  a  key  file, the CRC for each file is
           generated and you can choose to do  the  next  file  or  to
           quit.   The  CRC  is  shown  on  the 'Message:' line of the
           Generating dialog box.  When using a key file, the  CRC  is
           not shown.

           Before generating any CRCs you'll need to select some files
           and  also what method you're going to use.  The current CRC
           method is indicated in the 'Method' drop  down  combo  box.
           After  selecting  what  method  to  use you have to ways to
           select some files.  You can use the Files listbox to select
           file  individually, or the Include/Exclude edit controls to
           set up a 'File Inclusion Mask.'

           WinCRC can generate CRCs for all files  that  fit  a  given
           specification.   The  basic  logic  is to include any files
           that: have been selected in the file listbox, or those that
           match   the   Include  specification  but  not  an  Exclude
           specification.  The Include/Exclude controls  use  standard
           DOS  wildcards  and  can  contain  multiple  specifications
           separated by spaces.

           For example, to  include  all  files  with  .COM  and  .EXE
           extensions  type:  '*.EXE  *.COM'  (don't  type  the single
           quotes) in the Include edit control.   Remember  to  put  a
           space  between the two specs.  Now if you click 'GENERATE',
           CRCs for all .EXE and .COM files will be generated.  If you
           want to Exclude any files that start with the letter 'A' or
           'B', just enter 'A*.*  B*.*'  in  the  Exclude  line.   Now
           you'll  get  all  .EXE and .COM files that don't begin with
           either A or B.  Since files selected in the  Files  listbox
           are  always  included, you can override the Include/Exclude
           specifications for the directory WinCRC is currently in.



                                                                      




                                                                      


           If  you're  using  a  key  file,  right  after  you   click
           'GENERATE', you will be presented with the Generate Options
           dialog box.  This dialog contains two check boxes.  You can
           select  to  overwrite an existing key file and/or to record
           only file (no path) information in the key file.  Recording
           only  file info is useful if you're moving a group of files
           and don't know if they'll have the same path specification.
           The   file   SAMPLE.KEY  included  with  this  package  was
           generated without path info in the  key  file.   Note  that
           because  no  path  info is recorded it's not very useful to
           check Include Subdirectories; you'll just end up with  alot
           of File Not Found errors when you do a Verify.


        VERIFYING

           To verify files, you must have selected a key file.   Check
           the  Use  Key  File  check box and the 'VERIFY' button will
           become active. When you press 'VERIFY', CRCs for all  files
           in  the  key  file  are  generated and then compared to the
           stored values.  If the CRCs don't match or a file can't  be
           found,  the  error is printed on the 'Message:' line in the
           Verifying dialog.  The file in error and the error  message
           is  also  written  to  a  file  named WINCRC.ERR.  Like key
           files, WINCRC.ERR is a standard ASCII file.  Each time  you
           use Verify, WINCRC.ERR is overwritten.

           WINCRC.ERR is located in the working directory for  WinCRC.
           You  can  change the working directory by using the Program
           Manager.

           During verification, WinCRC will stop when it encounters an
           error.  You  can press 'NEXT' which continues but will stop
           with the next  error,  or  you  can  press  'FINISH'  which
           continues  without  stopping  until  all  files  have  been
           verified.  It you use the Finish  option,  you  can  always
           look in WINCRC.ERR to check on any verification errors.

           When using Verify with a key file that includes file  names
           but  no path information, you must be in the directory that
           contains the files to be verified otherwise WinCRC won't be
           able to find the files.

           There is one thing to note when using CRCs to verify files.
           Many  programs maintain configuration files.  SYSTEM.INI is
           an example of one of Microsoft Window's config files.  Some
           programs  actually write configuration information to their
           executable rather than in a separate file.   Of  course  if
           the file changes, so does the CRC. In these cases, the file
           has not been corrupted, rather the user has changed one  or
           more of the program's options.  To avoid having WinCRC flag
           these files, make your  changes  BEFORE,  using  WinCRC  to
           generate CRCs.


        CHOOSING A DEFAULT METHOD


                                                                      




                                                                      


           When you first run WinCRC, the default method  is  Checksum
           8.  WinCRC  can  maintain a different default method in the
           file WINCRC.INI.  To choose a  new  default  method  choose
           'DEFAULT',  select  whichever  method  you  want, and click
           'OK'.  Next time you run WinCRC, the  method  you  selected
           will  be the current one.  Note that choosing a new default
           method does not alter the current method selected for  this
           session.


        ALIASES

           A number of the methods WinCRC uses are  known  by  several
           different  names.   The  table  below  shows  the alternate
           names.

                Method                   Alias
                --------------------------------------------------
                CRC-16                   ARC, LHA, Zoo
                CRC-32                   ETHERNET
                ZModem                   PK-Zip, ARJ
                CRC-CCITT                SDLC, IBM
                CRC-CCITT Reverse        SDLC Reverse, IBM Reverse

           Do not confuse CRC-32 with PK-Zip or ARJ.  PK-Zip  and  ARJ
           precondition  the  CRC before and after generation.  CRC-32
           does not. If you use CRC-32 you  won't  get  the  same  CRC
           values that PK-Zip or ARJ generate.


        KEYBOARD USERS

           If you're using a keyboard rather than a mouse, all of  the
           Window's  controls  respond in their default fashion.  I.e.
           to "press" a button, tab to it and  then  press  the  space
           bar.   The one exception it the Directories list box on the
           main window.  Since there is no button to switch to another
           directory, this list box uses the <RETURN> key.  Hightlight
           the directory you want (using the arrow keys  or  spacebar)
           and  then  press  <RETURN>.   WinCRC will switch to the new
           directory.


        A NOTE ON MD5

           As  of  version  1.0  of  WinCRC,  I  am   considering   my
           implementation   of   the   Message   Digest   5  algorithm
           experimental.  Although the algorithm is similar to MD4,  I
           didn't  have  any  other  working  code  to  verify the MD5
           results that WinCRC generates.  If you're not  getting  the
           MD5 output that you expected, this is probably the reason.


        REGISTRATION

           WinCRC is not a free or public domain program.  You may use


                                                                      




                                                                      


           it  for  a  period  of  thirty  (30)  days  for  evaluation
           purposes.   To  continue  using  it  after  that,  you must
           register the software.  The more people who  register,  the
           more  incentive  I have to update the program and implement
           user suggestions.  Makes sense, huh?

           To register, send a check or money  order  for  US  $15.00,
           payable to Eric Roe, to the following address:

                Eric Roe
                WinCRC Registration
                3137 Briarcliff Avenue
                Vestal, New York  13850-2859

           Also, if you have any comments and/or suggestions on how  I
           can  improve  WinCRC  you  can send them to me at the above
           address.   I  can  also   be   reached   via   e-mail   at:
           ericroe@aol.com.


        DISTRIBUTION

           WINCRC.EXE and associated help files and documentation  are
           Copyright  (c) 1994 by Eric Roe, all rights reserved.  They
           may not be distributed in an incomplete or  modified  form,
           nor  can  they  be  sold  for  profit without prior written
           consent of the author.

           If  this  software  is  to  be  distributed  it   must   be
           distributed as a package consisting of the following files:

                WINCRC.EXE
                WINCRC.HLP
                WINCRC.DOC
                WINCRC.ERR
                SAMPLE.KEY
                REGISTER.DOC
                README.1ST

           Software dealers  and  shareware  libraries  may  charge  a
           minimal  copying/disk  fee  for  the  above  package not to
           exceed US $8.00.


        DISCLAIMER

           This software, WINCRC.EXE and its associated  documentation
           and  help  files,  is  provided on an "as is" basis without
           warranty of any kind, express or  implied,  including,  but
           not  limited  to,  implied  warranties  of merchantability,
           fitness  for  a  particular  purpose,  functionality,  data
           integrity, or data protection.  Persons using this software
           bear all risk as to the  quality  and  performance  of  the
           software.   The  author  will  not  be liable for direct or
           indirect damages or data  loss,  even  if  the  author  was
           informed of the possibility of such damages or data loss.


                                                                      




                                                                      


           Suggestions, improvements, diagrams, and other documents or
           documentation  sent  to  the  author become property of the
           author.  No reimbursements or remuneration will be made.