BOBSLED version 1.09 Help Text (unformatted)                      
BOBSLED Copyright (C) 1994 Full Motion Net
05.10.94, 07.05.94

     The following text references all the objects  and  commands  that
     concern the program and or the environment BOBSLED.   This text is 
     unformatted,  and  moves  from topic to topic.  It is included, by 
     request,  as a way  to  quickly  understand  BOBSLED's  functions, 
     without using BHELP.EXE on a per-item basis.


                             -START OF HELP.DOC-



*    Command Line Syntax:      

     By typing:  "BOB x:\path\filename.ext"  you can open  a  file  and 
     start BOBSLED.   "x" is the drive.   If  the  file  resides in the 
     current directory, you need  not  include  the drive and path.  If
     you do not supply an extension,  BOBSLED  will  search for first a
     Project file matching the specification, then a BPS file.
     
     
*    File Formats:

     BOBSLED loads 3 types of files, identified by their extension.

     Project File            NAME.PRJ        List of Source Files

     Source File             NAME.BPS        Module and Subroutines

     Text File               NAME.TXT        Supplemental Text


     A Project file, simply contains a list of Source, Include, and Text 
     files that  you  wish  to open at  the  same  time during a BOBSLED 
     session.  For example:

          MYPROJ.PRJÄÄÄÄ¿
                        ÀÄÄÄÄÄ>     MYPPL.BPS
                     contains       D:\STUFF\STUFF.BPS
                                    f:\when\TIME.BPS
                                    C:\DATE.BPS
                                    COOL.TXT

          MYPPL.BPS                 Since this is the first  file to be 
                                    loaded,  it  will be considered the 
                                    startup file, or main module.

          D:\STUFF\STUFF.BPS        All other sequential BPS files will
          f:\when\TIME.BPS          be  considered  Include  files,  or
          C:\DATE.BPS               rather    subroutines    that   are
                                    called externally from  MYPPL.BPS.
          
          COOL.TXT                  Text  files  can  be   loaded  with
                                    the project, however  they  are not 
                                    parsed,  even  if their  text  con-
                                    tains valid subroutines.
          
          If a file listed in the Project File does not  include a full 
          path, it will be searched for in the current directory.

                    file extension>ÄÄ¿
                     filename>ÄÄ¿    ³
                    path>ÄÄ¿    ³    ³
               drive>ÄÄ¿   ³    ³    ³
                       f:\when\TIME.BPS
          
          When  listing  files, it is imperative to include proper file 
          extensions.
          
          BPS File Format is equivalent to  a  PPS  Source  File,  with
          the exception, that a BPS  format  incorporates  the  use  of
          actual subroutines.   PPS files use Calls to external Include 
          Files, and GOSUB/RETURN blocks.

          For  the  benefit  of structured programming BOBSLED exploits 
          the use of  "CALL/SUB/END SUB,"  routines,  while maintaining
          full  compatibility  with  the PPL language,  through the use
          if its Translate utility.  See below example:

          MYPPL.BPS parsed toÄ¿ 
                              ÀÄ>  MYPPL.MOD    and     MYSUB.SUB
          
          Main Module>ÄÄÄÄÄÄ¿
                            ÀÄÄ>   Module level code    MYSUB SUB
                                   ..                   ..
                                   ..                   ..
                                   ..                     code block
                                   ..                   ..
                                        CALL MYSUB      ..
                                   ..                   END SUB
                                   ..
                                   ..

          When parsed, MYPPL.BPS will be split  into  its  main  module
          and subsequent subroutines.  The main module  will  be  temp-
          orarily stored as MYPPL.MOD,  and  subsequent  subroutines as
          the SUBNAME.SUB.

          When MYPPL.BPS is Translated to PPS format,  BOBSLED  changes 
          "MYSUB SUB" to ":MYSUB_SUB."  The "CALL MYSUB"  statement  is 
          changed to "GOSUB MYSUB_SUB," and the "END SUB" to  "RETURN." 
          All  subroutines  are  appended  to  the end of the MYSUB.MOD 
          file.  The  file  is  renamed  and  copied  to the  directory 
          "\MYPPL\MYPPS.PPS,"  off the  BOBSLED  directory.  See  below 
          example:
          
          Original Format:       Where C:\ is the BOBSLED directory.
          
          C:\MYPPL.BPS
          
          C:\TEMP\MYPPL.MOD       C:\TEMP\MYSUB.SUB
          Module level code       MYSUB SUB
          ..                      ..
          ..                      ..
          ..                        code block
          ..                      ..
          CALL MYSUB              ..
          ..                      END SUB


          Translated to:

          C:\MYPPL\MYPPL.PPS
          
          Module level code    
          ..                   
          ..                   
          ..                   
          ..                   
          GOSUB MYSUB_SUB      
          ..                   

          :MYSUB_SUB
          ..
            code block
          ..
          RETURN
          
          Note:  The use of  Translate does  not  affect  the  original
                 BPS  file.  In  this  case,  "MYPPL.BPS"  would remain 
                 intact,  such that it could be  reloaded into BOBSLED, 
                 for   additional   editing.    The   translated   file 
                 "MYPPL.PPS" can not be loaded into BOBSLED.
                 
                 Future versions  of  BOBSLED  may  include  a  reverse
                 translator, however one is not available at this time.
     


*    PLEASE BE ADVISED:  07.05.94 changes will now truncate a subroutine
                         name to its first 8 characters.


     
*    Error Tones:

     Low tone generally means selection is unavailable, function  can't
     be preformed or is unnecessary, function was aborted or  an  error
     has occurred.

     High tone means "OK," function completed, selected, or done.
                      

*    Topic Conventions:

          Focus is simply defined as the active object or wherever  the
          current cursor position is.

          ()          The letter that is highlighted.
          ...         Indicates that the item will further  prompt  you 
                      with an additional selection box.

          -           Separation bar.
          
          [ NONE ]    While  this  Menu  Item  is  define as the Active 
                      Attributes  Function,  it will change accordingly 
                      to  the  current  Project,  the  current  Startup 
                      Module, or "NONE" if no files are loaded.
          
          "position"  Usually  refers  to  current  cursor position, or 
                      last cursor  position  if  focus  is no longer on 
                      the text editor.

          ^ caret     used instead of "Control" or Control Key.

          "Hot Key"   quick combination of  keys to access a procedure.  
                      Some Hot Keys: ^P, ^S, F1 - F12, ^F1 - ^F12, ETC.


*    Main Form Commands:

     Ú´                             BOBSLED                            Ã¿
     ³  ð  File  Edit  Search  Tools  Run  Desktop  F1ùHelp  [ NONE ]  ³
     ³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³
     ³³-                                       ³   No Modules Loaded ³³
     ³³                                       Û ³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³³
     ³³                                       ° ³³ Untitled          ³³
     ³³                                       ° ³³                   ²³³
     ³³                                       ° ³³                   °³³
     ³³                                       ° ³³                   ³³
     ³³                                       ° ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³³
     ³³                                       ° ³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³³
     ³³                                       ° ³³                   ³³
     ³³                                       ° ³³                   ²³³
     ³³                                       ° ³³                   °³³
     ³³                                       ° ³³                   °³³
     ³³                                       ° ³³                   °³³
     ³³                                       ° ³³                   ³³
     ³³                                        ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³³
     ³À<²°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°>Ù ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³
     ³ Local Message Area....................  265 | 1 | 0  Free: 32500³
     ³ Ctrl-E Min  Blanker  Line Draw  Goto Block  ROW: 1 COL: 1   CNI ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
                   (form shown smaller than actual size)
     
*    Form Operation:
     
          The  entire  BOBSLED Form may be moved or repositioned on the
          display  screen.  Simply  Left Click the Border and Drag to a
          new location.
     
     
     Key Commands:   TAB, SHIFT + TAB

     Tab and Shift + Tab  will set Focus to the next available  object.
                          Tab orders forward and Shift + Tab reverse.

     Left Clicking        the  Mouse  on any object will also set focus 
                          to that object and or execute its function.
     

     Menu Operation:
     
     ð   File   Edit   Search   Tools   Run  Desktop  F1ùHelp  [ NONE ]

     Key Commands:   ALT, ESC, ARROW KEYS, ENTER

     Alternate Key                   activates the menu bar.
                        
        Pressing the Alternate Key and the highlighted letter of a menu 
        item  will  also  select it.  The next level of items will drop  
        down for selection,  or  execute  its function if no additional 
        items exist.

     Left or Right Arrow Keys        highlights or specifies which menu
                                     item is active.

        Using  the Down Arrow Key or the Enter Key while a menu item is 
        selected, will drop down the next level of items for selection, 
        or execute its function if no additional items exist.

     Escape                          will  deselect  the  menu  bar  or 
                                     close a  previously  dropped  down 
                                     menu box.


     Mouse Commands:

     Left Clicking                   any  item  selects  it  and either 
                                     executes  its  function  or  drops 
                                     down its respective selection box.

     Right Clicking                  the Mouse is equivalent to pressing
                                     the Escape key.  See above.
     

*    Menu Definition:
     
     ð   File   Edit   Search   Tools   Run  Desktop  F1ùHelp  [ NONE ]

     If a menu item or selectable item in a drop down box  is  followed
     by  a  Shortcut  Key  then  its  function  may be executed without 
     opening  the  drop  down  box.  Simply  press  the appropriate key 
     combination.

          Drop Down Box        
          ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
          ³  (O)pen Project...    ³  (O) The "O" is highlighted.
          ³  Sa(v)e Project     F2³    
          ³  -                    ³  ... The function will display a 
          ³  (N)ew Module...      ³      prompt for additional choices.
          ³  A(d)d Module...      ³ 
          ³  (R)emove Module...   ³  F2  is the Shortcut Key.
          ³  (S)ave Module        ³ 
          ³  Save (A)s...         ³  -   is a separator.                         
                           
    
*    ð  About:
          
          ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
          ³                       BOBSLED                       ³
          ³                Bob's Language Editor                ³
          ³           Copyright c 1994  Full Motion Net         ³
          ³          24 Hour Support BBS  (609) 625-4475        ³
          ³                                                     ³
          ³ Authentic PC Board Documentation Used by Permission ³
          ³   Copyright c 1993  Clark Development Corporation   ³
          ³                      ÚÄÄÄÄÄÄÄÄ¿                     ³
          ³                      ³   OK   ³                     ³
          ³                      ÀÄÄÄÄÄÄÄÄÙ                     ³
          ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
          
     Pressing Escape, Enter, or Left Clicking the  "OK"  Button  closes
     the box.  Focus returns to the previously active control.
     


     
*    (F)ile Summary:
     
     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³  (O)pen Project...    ³ Loads a new BPS, TXT, or PRJ file.
     ³  Sa(v)e Project     F2³ Saves all the current loaded files.
     ³  -                    ³
     ³  (N)ew Module...      ³ Clears memory, loads new file.
     ³  A(d)d Module...      ³ Loads files, existing files remain.
     ³  (R)emove Module...   ³ Unloads currently selected module.
     ³  (S)ave Module        ³ Saves currently selected module.
     ³  Save (A)s...         ³ Saves selected module as specified.
     ³  -                    ³
     ³  (P)rint...           ³ Sends selected output to a device.
     ³  MS-DOS S(h)ell       ³ Drops to DOS without quitting BOBSLED.
     ³  E(x)it               ³ Quits BOBSLED, prompts to save if needed.
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ 
                     
        If  a  prompt  to  Save  is displayed, then your work more than 
        likely needs to be saved.  The  "Saving"  message  in the Local 
        Message Area, only  saves temporary files for internal use.  If 
        you do not get a prompt to save then you don't need to.

          
     
*    (E)dit Summary:

     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³  (U)ndo               ³ Editor contents prior to last function.
     ³  -                    ³
     ³  Cu(t)                ³ Remove, copy selected text to Clipboard. 
     ³  (C)opy               ³ Copy selected text to Clipboard. 
     ³  (P)aste            ^P³ Insert selected text at cursor position. 
     ³  (A)ppend             ³ Add selected text to Clipboard contents. 
     ³  (D)elete             ³ Erase selected text.
     ³  -                    ³
     ³  (N)ew Sub...       ^S³ Create new subroutine, name as specified.
     ³  (M)ove Sub...        ³ Move a subroutine from Module to another.
     ³  Copy (S)ub As...     ³ Duplicate selected subroutine.
     ³  (R)emove Sub...      ³ Delete selected subroutine.
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

     

*    (S)earch Summary:

     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³  (F)ind...             ³ Preforms a specified search for a string.
     ³  (R)epeat Last Find  F3³ Continues an initial search from position.
     ³  (C)hange...           ³ Replaces found string with specified text.
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
      
     

*    (T)ools Summary:

     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³  PPL (C)ommand List    F4³ Display PPL Commands in selectable box.
     ³  PCB (M)acro List      F5³ Display @Macros in a selectable box.
     ³  -                       ³
     ³  (S)hell to PCB Editor F6³ Run specified editor, from BOBSLED.
     ³  -                       ³
     ³  Show (C)lipboard      F7³ Display the contents of the Clipboard.
     ³  (T)ime / Date Stamp   F8³ Insert the CMOS Time & Date at current 
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ cursor position.
     
     
      
*    (R)un Summary:

     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³  (S)yntax Check          F9³ Scan  for  syntax errors in window.
                                    Module  or  Subroutine name must be
                                    highlighted in bottom List Box.
     
     ³  (T)ranslate...         F10³ Convert BPS Format to PPS Format.
     ³  (C)ompile, Make PPE... F11³ Compile PPS File to PPE File.
     ³  (R)un PPE              F12³ Execute PPE in PC Board, from BOBSLED.
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
      


*    Des(k)top Summary:

     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³  (D)isplay Colors... ³ Change object or display colors.
     ³  (E)nvironment...    ³ Modify file locations  for  compiler  and
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ PCB Editor.
      


     
*    F1ù(H)elp Summary:
     ÚÄÄÄÄÄÄ¿
     ³ HELP ³ If the  current  cursor  position  of the  editor is on a
     ÀÄÄÄÄÄÄÙ command word, then Help will display its usage. If cursor
              is on white space, Help Contents will be displayed.
              See Help on Help.

              If  a  function  box was  displayed  prior to pressing F1
              then Help will be displayed for the function of focus.
      
              If the  Editor  box is empty, F1 will display Help on the
              Editor's available commands.

              All  command  help  requests display in the local message
              area; identifying the verbose request.

              See also:  The  file  "Readme.txt,"  which  contains some
              information about BOBSLED, not included in Help.    
     

*    Attributes of the Project:
     
     ([) MYSTUFF.PRJ ] Active Attributes Summary
     
     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³  There are...                                              ³
     ³  N Modules and N Subroutines...                            ³
     ³  These N files, use approximately N Bytes.                 ³
     ³                                                            ³
     ³  This information was updated on the last Processing Run.  ³
     ³                                                            ³
     ³                           ÚÄÄÄÄÄÄÄÄ¿                       ³
     ³                           ³   OK   ³                       ³
     ³                           ÀÄÄÄÄÄÄÄÄÙ                       ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
     
     Where "N" is a number.  Indicates number of Modules and Subroutines
     currently loaded in BOBSLED, and the amount of bytes that they use.
     If you are using the DOS  command APPEND and the "/PAGE:ON" conven-
     tion, then the number of modules or subroutines loaded may be wrong.
     Simply set to "/PAGE:OFF" and this should correct the problem.

     The last processing run was the last time BOBSYS was called.
     
     See: Main Form Commands  Topic Conventions  for help on title.

     Pressing Escape, Enter,  or Left Clicking the  "OK"  Button closes
     the box.  Focus returns to the previously active control.
     
     
*    Text Editor Commands:
     
           ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ 
     Row 1 ³_  Blinking underline is the current               
           ³   cursor position.                               ±<current 
           ³                                                  ° position
           ³                                                  ° 
           ³                                                  ° 
           ³                                                  ° 
           ³                                                  ° 
           ³                                                  ° 
           ³                                               Vertical
           ³                                                Scroll
           ³                                                 Bar
           ³                                                  ° 
           ³                                                  ° 
           ³                                                  ° 
           ³                                                  ° 
           ³                                                  ° 
    current³                            Horizontal Scroll Bar  
    position<±°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°>Ù

      Column 1..............................................2048 +
   
      A  warning  tone  will  sound for each character that exceeds the 
      2048 character limit, per line.
                   

     Key Commands:   ALL KEYS, SHIFT STATES AS DEFINED

     Left, Right, Up, Down Arrow     moves 1 space in respective direction.

     Control + Left or Right Arrow   moves 1 word in respective direction.

     Home                            moves to beginning of row.
     Control + Home, once            moves to beginning of block.
     Control + Home, twice           moves to beginning of window.

     End                             moves to end of row.
     Control + End, once             moves to end of block.
     Control + End, twice            moves to end of window.

     Page Up                         moves one screen up. 
     Page Down                       moves one screen down.

     Insert                          if  "ON,"  will  put  typed text at
                                     current  cursor  position,  pushing
                                     any existing text to the right.

     If Insert is  "OFF,"  then any  text at the current cursor position 
     will be  overwritten.  When  Insert  is  "OFF,"  the cursor changes 
     to a blinking "÷71Û" character.

     Delete                          removes a character or space at the
                                     current  cursor  position, any text
                                     right  of  this  position will move 
                                     one space left.

     Control+ Delete                 erases text  or  space from current
                                     cursor  position  to the end of the
                                     row.

     Backspace                       removes a character or space at the
                                     current  cursor  position, any text
                                     right  of  this  position will move 
                                     one space left.  Cursor position is 
                                     moved one space left.

     Control + Tab                   inserts 5 spaces right.

     Enter                           carriage return, line feed.

     Shift + Arrows                  selects text in respective direction,
                                     selected text becomes highlighted.
                        
     Control + Shift + Grey Key      selects text and carries out the grey
                                     key's function.

     Pressing an arrow key after text is selected will deselect the text.
     If  text  is  selected,  pressing  delete, or any character key will 
     erase  the  selected  text,  or replace  the selected text with that 
     character.

     Shift + Delete                  when  text  is  selected, will erase 
                                     the text, and backspace 1 space.

     Control F1 - F12                See:  Line Draw
     
     Alphanumeric Keys               allow entry of letters and numbers.
     
     
     Pause                           halts  execution,  press  any key to
                                     continue.

     Mouse Commands:

     Left Clicking Text              sets  the  cursor  position  to the
                                     mouse current cursor position.

     Left Click & Drag               selects text in respective position.
                        
     Left clicking while text is selected deselects text.  Left clicking 
     and dragging beyond the vertical boundaries of the  text  box  will 
     cause the text box to scroll in that  respective  direction,  while 
     text is being selected.

     
     Caps Lock                       toggles case of letter keys.
     
     Number Lock                     toggles use of number pad.  
     
     Pressing the  Alternate  Key + an ASCII number code will print the 
     respective   ASCII  character  at  the  current  cursor  position.  
     Toggle ON the Number Lock, use the Number Pad. See:  Ascii Chart
     
     
*    Scroll Bar Usage:

     Left Clicking Horizontal and Vertical Scroll Bars
                                      
                                                         s 
                                                         ±.
                                                         °. 
                                                         °. 
                                                         °. 
     <±°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°>  s 
      s..............................................s

      Left clicking a scroll bar at the "s" marks will cause the screen
      to scroll one position towards its respective direction.

      Left clicking a scroll bar at the "." marks will cause the screen
      to scroll to the selected position.

     
*    Active Module/Subroutine List Box:

     Opening Bobsled with no       After "MYPPL.BPS" was
     files loaded.                 loaded.
               
     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³   No Modules Loaded  ³      ³     Active Module    ³  
     ³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³      ³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³
     ³³ Untitled           ³      ³³ MYPPL.BPS          ³ Listed Modules
     ³³                    Û³      ³³                    Û³ Text Files
     ³³                    °³      ³³                    °³
     ³³   upper list box   ³      ³³                    ³
     ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³      ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³
     ³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³      ³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³
     ³³                    ³      ³³ MYPPL.BPS          ³ Module
     ³³                    Û³      ³³    MYSUB1          Û³    Subroutines
     ³³                    °³      ³³    MYSUB2          °³    ..
     ³³                    °³      ³³    MYSUB3          °³    ..
     ³³                    °³      ³³    MYSUB4          °³    ..
     ³³                    °³      ³³    SENDMAN         °³    ..
     ³³                    °³      ³³                    °³    ..
     ³³                    °³      ³³                    °³    ..
     ³³   lower list box   ³      ³³                    ³    ..
     ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³      ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ 

     All loaded Modules and Text Files in the upper  box are listed  in
     the load order.  The top  Module  becomes  the  Startup file.  The
     startup file will be  named  with  the  extension  "PPS"  after  a
     Translation, all  subsequent Modules will be named using the "INC"
     extension.  Should you prefer a different order, save loaded files
     as a Project and or change the load order in the Project file.

     As each item in the upper list box is selected, the lower list box
     reflects its name  and  any subroutines parsed in that Module.  As
     an item in the lower list  box is selected its contents are loaded
     into the editor text box.  Between loading selected subroutines or
     modules, BOBSLED will save the  current contents of the editor box
     back to its corresponding module or subroutine temporary file. You
     must use the Save Functions in order to permanently save your work,
     saving to temporary files is only for BOBSLED's internal use.
     
     On each occurrence of a blockset  change  or attempt to exceed the 
     window's content's length,  BOBSLED will  also preform a temporary
     file save.
     
     Key Commands:   ALL KEYS, SHIFT STATES AS DEFINED

     Left, Right, Up, Down Arrow     moves 1 item in respective
                                     direction.
     
     Home                            moves to beginning of list.
     End                             moves to end of list.

     Page Up                         moves one list length up. 
     Page Down                       moves one list length down.

     A to Z, or a to z               moves  to the  item  whose  first
                                     letter matches the pressed key.

                                     Subsequent presses of a key  that
                                     matching  several  items  in  the
                                     list,  will move the selection to
                                     the  next  matching  item  in the
                                     list.

                                     In the example above, pressing "M" 
                                     or  "m"  will  move  the selector
                                     between  the first 5 items in the
                                     list.

     Tab and Shift + Tab             will set Focus to the next avail-
                                     able  object.  Tab orders forward
                                     and Shift + Tab reverse.
     
     Mouse Commands:

     Left Clicking Item              selects the Item.

     Left Click & Drag               scrolls List in respective direction.

                                     Left clicking and dragging  beyond
                                     the  vertical  boundaries  of  the
                                     list box will  cause  the list box
                                     to  scroll  in   that   respective
                                     direction.   Upon   releasing  the
                                     button, the item that is selected, 
                                     will be loaded.
     


*    Ctrl-E Min:
  
     This function will widen the text editor box to 76 columns, or if
     at 76 columns, it return to its normal width of 50 columns.  When
     the editor box is maximized,  "Ctrl-E Min"  becomes  "Ctrl-E Max"
     and the Active Module List Box is no longer in view.

     Key Commands:
                        
     Control + E                     activates function.
     
     Mouse Commands:

     Left Clicking Item              activates function.
     
     

*    Blanker:
  
     This function hides the BOBSLED form, until a key is pressed. Use
     as an "on demand" screen saver.
     
     Key Commands:
                        
     Control + B                     activates function.
     
     Mouse Commands:

     Left Clicking Item              activates function.
  


*    Line Draw:

     Activating this function displays/hides the following line:

     ControlÿF1:ÚÿF2:¿ÿF3:ÀÿF4:ÙÿF5:ÄÿF6:³ÿF7:ÃÿF8:´ÿF9:ÁÿF10:ÂÿÿF11+ÿF12-

     Note:   It is not required to have the set line displayed in order
             to print the set characters.  The display only allows  you
             to view the selected  set  and  corresponding  characters.
             Control + F#,  works  full  time and is independent of the
             display line.  See below for Key Commands.

     Sets:
     Set  1        F1:Ú F2:¿ F3:À F4:Ù F5:Ä F6:³ F7:Ã F8:´ F9:Á F10:Â 
     Set  2        F1:É F2:» F3:È F4:¼ F5:Í F6:º F7:Ì F8:¹ F9:Ê F10:Ë 
     Set  3        F1:Õ F2:¸ F3:Ô F4:¾ F5:Í F6:³ F7:Æ F8:µ F9:Ï F10:Ñ 
     Set  4        F1:Ö F2:· F3:Ó F4:½ F5:Ä F6:º F7:Ç F8:¶ F9:Ð F10:Ò 
     Set  5        F1:Å F2:Î F3:Ø F4:× F5:Ä F6:º F7:Ç F8:¶ F9:Í F10:ð
     Set  6        F1:° F2:± F3:² F4:Û F5:ß F6:Ü F7:Ý F8:Þ F9:þ F10: 
     Set  7        F1: F2: F3: F4: F5: F6: F7:  F8:
 F9: F10:
     Set  8        F1:« F2:¬ F3:¨ F4:­ F5:� F6: F7:  F8:® F9:¯ F10:M
     Set  9        F1: F2: F3: F4: F5: F6:E F7: F8:- F9: F10:   
     Set 10        F1:  F2:¦ F3:’ F4:‘ F5:� F6:Ž F7:ƒ F8:„ F9:… F10:† 
     Set 11        F1:‚ F2:ˆ F3:‰ F4:Š F5:� F6:Œ F7:� F8:‹ F9:¡ F10:S 
     Set 12        F1:€ F2:‡ F3:› F4:” F5:• F6:™ F7:¢ F8:å F9:é F10:“ 
     Set 13        F1:š F2:— F3:– F4:£ F5:æ F6:¤ F7:¥ F8:œ F9:˜ F10:ž 
     Set 14        F1:§ F2:¦ F3: F4:â F5:© F6:ª F7: F8: F9: F10:ì
     Set 15        F1:­ F2:à F3:á F4:‡ F5:ã F6: F7: F8:æ F9:ç F10:è 
     Set 16        F1:› F2:ê F3:Ÿ F4:ä F5:í F6:î F7:ï F8:ñ F9:ò F10:ó 
     Set 17        F1:ô F2:õ F3:ö F4:¨ F5:  F6:ù F7:ú F8:û F9:ü F10:ý 
     
                   M = Ascii # 255  White space character        
                   S = Ascii # 32   True space character
                   E = Ascii # 26   End of File Marker, "right arrow" 

     Note:   In certain programs you may wish to use a 255 character in
             lieu of a space character, therefore it is provided.
     
     Key Commands:
                        
     Control + L                     displays/hides set. 

                                     Function is always active, even if
                                     set is not visible.
     
     Control + F1 - F10              draws respective character.
     Control + F11                   toggles sets forward.
     Control + F12                   toggles sets backward.
     
     Mouse Commands:

     Left Clicking Item              activates function.
     


*    Goto Block:

     If more than 1 Block Set is available, use of this function allows
     you to quickly move to any position in a large document.  You will
     be prompted with an input box, specifying the range of  selection.
     Type  in  the  number  of  the block to goto, press Enter.  Cancel
     aborts the function.
     
     Blocks are numbered  0 to 999.  For a more in depth explanation of
     blocks and block sets, See:  Block Sets
     
     Key Commands:
                        
     Control + G                     activates function, if available.
     
     Mouse Commands:

     Left Clicking Item              activates function.



*    Block Sets:

     An integral part of the BOBSLED Text Engine  makes  use  of  Block
     Sets for several reasons.

          1.      Allows huge Ascii files to be opened and parsed.

          2.      Allows quick access,  to all parts of a file, without
                  repeatedly using the Page Up or Page Down Keys.

          3.      Allows  a  huge  Ascii file to average it size, as it
                  grows.   Therefore  never  exceeding  the  amount  of
                  environment space.

          4.      Consistently updates its temporary files as the cursor
                  position changes in a document.  
               
                  Should BOBSLED ever "lock up" or "crash" on the system,
                  its internal temporary files may  still  be  retrieved,
                  simply by restarting the program,  or from the command
                  line.  This feature is similar to an automatic backup.
               
          5.      Block Sets are fundamentally  determined when a  file
                  is first opened, or reloaded  into  the  text  editor
                  box.  See:  Active Module List Box
               
                  A  Block  Set is determined by weighing  access speed
                  against optimal block size. Some opened files may not
                  pass the Block Set qualification,  and  therefore are
                  loaded into Block 0.

     Each  Block  Set  consists  of 3 Blocks, each approximately 4 K in
     size.  As you scroll through the editor box in a  large  document, 
     the Blocks of the current Block Set change.

     BOBSLED allows up to 1000 Blocks, numbered 0 - 999, for any opened
     file.  Files that require more than 1000  Blocks will abort during
     the load procedure.  Generally  any  file less than  3.5 megabytes
     will load into  BOBSLED.  Please keep  in mind that the larger the
     file  the  more  time  it  will require to process.  A file over a
     megabyte will  take  several  minutes  to  parse, even on a 486-50
     machine.

     The following graphical example further explains this concept:
                                                      
                                                      Set 1
     ÚÄÄÄÄÄÄÄÄÄÄÄ¿                            Block 0 ÄÄÄÄ¿ Set 2
     ³ 84 K File ÅÄÄÄÄ¿   Parsed to           Block 1 ÄÄÄÄÅÄÄÄÄÄÄ¿  Set 3
     ÀÄÄÄÄÄÄÄÄÄÄÄÙ    ÀÄ> 21  4K Blocks ÄÄÄ>  Block 2 ÄÄÄÄÁÄÄÄÄÄÄÅÄÄÄÄÄÄÄ¿
                                              Block 3 ÄÄÄÄÄÄÄÄÄÄÄÙ       ³
                                              Block 4 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
                                              Block 5 ...and so on...
     Block Set 1 uses Blocks 0 - 2            Block 6
     Block Set 2 uses Blocks 1 - 3            Block 7
     Block Set 3 uses Blocks 2 - 4            Block 8
     Block Set 4 uses Blocks 3 - 5            Block 9
     ETC.                                     ..TO...
                                              Block 21


     Concerning the Goto Block Command, the Block to be accessed should
     be the Top Block in a Block Set.  It is perhaps  easier  to  press
     Control + Home twice, or Control + End twice,  to get to the first
     or last Block Set than to use the Goto Block Command.

     In  the  example,  if  you  wanted  to  jump  to the middle of the 
     document, you should use 9 or 10 as a Block number to goto. If you
     specify  Block  10,  Block 10  is the Top Block,  Block 11  is the
     Middle Block, Block 12 is the Bottom Block, of the Block Set.  The
     Row  indicator  will update, based on your current position in the
     file,  therefore  by  using a couple of Page Ups or Downs, you can
     get to the precise point in the file, very quickly.

     Block 10 is the 11th Block of the document. 11 X 4K = 44K. 44K is
     about half the file size, of 84K.

     As your document grows in size, and each  time  you  either  switch
     the editor's contents, using the Active List Box Control, or simply
     by scrolling through  the  editor  box,  your  Blocks will begin to 
     average out the data in the file.

     For example:

          Original document: 84K  21 4K Blocks.
          
               After typing in more text the new size is 104K.

          Updated document: 104K  21 5K Blocks.

               You switch documents, or reload the file.

          Updated document: 104K  26 4K Blocks.

     To determine the middle block of any loaded file, use this method:
                     
                     ^END, twice
                      (Top Block + 3) / 2
                      + or - 1

     The Status / Message Area will inform you of the current Top Block
     and the Row number of the Block Set you are in, and the Row number
     of the next Block Set Change.

                     ÚÄÄ> Row number of the next Block Set Change.
                     ³
                     ³    ÚÄÄ> Row number of the Current Block Set 
                     ³    ³
                     ³    ³   ÚÄÄ> Top Block
                     ³    ³   ³
                    265 | 1 | 0  Free: 20400
          Goto Block  ROW: 1 COL: 1      CNI 

     The ROW: COL: indicators display the current position of the cursor
     based on the document, not the Block Set.

     Free: 20400 indicates the amount of free space left in a Block Set
     before an average or reload must take place.  This figure is based
     on the maximum limit of 32,500 bytes in the editor box.

          32,500 - 20,400 = 12,100

          12,100 = number of bytes that the current block set occupies, 
          or  the  number  of  bytes  currently contained in the editor
          box.

     Visual Basic for DOS, allows a maximum of 32,768 characters, to be
     entered into its Text Box Objects.  BOBSLED uses 268 bytes of this
     for overhead, thus we have the 32,500 byte figure.

     If you start BOBSLED,  with no opened files,  there are no Blocks,
     or Block Sets, therefore no Block Information will be displayed. 
     
     If  the  Indicator  "Block 0 of 0"  is displayed, this informs you
     that the  current  loaded  file  was not large enough to be parsed
     into more than 1 Block or Block Sets.  

     The  Goto Block Function may only be used if the number of current
     Blocks  is  greater  than  3,  or  there is more than 1 Block Set.
     Attempting to use this Function,  when  it  is  not available will
     generate a low error tone.

     The  temporary  Block  Set files are maintained in a directory off
     your main BOBSLED  directory,  called  "BLOCKS."   The  files  are
     labeled "BLOCK.000"  to  "BLOCK.NNN," where "NNN" is the number of
     the last Block.
     
     Modules  and  Subroutines  are  parsed  and stored in the  "\TEMP"
     directory, off BOBSLED's  main  directory.   If  you  attempt  to
     manually  rebuild  files,  you  main  find  everything  that  was
     loaded  here.   Modules  will  have   the  extension,  "MOD"  and
     Subroutines,  "SUB."    TXT  files  are  simply  copied  to  this
     directory.  When BOBSLED quits normally, both the BLOCKS and TEMP
     directory are erased.  If BOBSLED crashes they remain.



* Status / Message Areas:
  
  Free Bytes Remaining in Editor Box or Block Set, before Reloading. <ÄÄ¿
                                                                        ³
  Top Block. <ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿            ³
                                                           ³            ³
  Row number of the Current Block Set. <ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿   ³            ³
                                                       ³   ³            ³
  Row number of the next Block Set Change. <ÄÄÄÄÄÄ¿    ³   ³            ³
                                                  ³    ³   ³            ³
  Warning, or Status Messages,                    ³    ³   ³            ³
  appears in Red, informs you                     ³    ³   ³            ³
  of BOBSLED's current action.                    ³    ³   ³            ³
      ³                                           ³    ³   ³            ³
      ³                                           ³    ³   ³            ³
  { local message area.............. }           265 | 1 | 0   Free: 20400
  Ctrl-E Min    Blanker    Line Draw   Goto Block  ROW: 1 COL: 1       CNI 
    ³             ³          ³           ³            Cursor           Key  
    ³             ³          ³           ³           Position         State
    ³             ³          ³           ³
    ³             ³          ³       Quickly accesses a specific Block Set.
    ³             ³          ³
    ³             ³        Displays Character Sets.
    ³             ³
    ³           Hides Form, until a key is pressed.
    ³
  Widens Editor Text Box.
  
     If you start BOBSLED, with no opened files,  there are no  Blocks,
     or Block Sets, therefore no Block Information  will be  displayed. 
     
     If  the  Indicator  "Block 0 of 0" is displayed, this  informs you
     that  the  current  loaded file was not large enough to be  parsed
     into more than 1 Block or Block Sets.  
  
     When  text  is being selected, the ROW: COL: indicator  changes to  
     SELECTING TEXT,  and  is  displayed in Red, until the text  is de-
     selected and/or the current cursor position has changed.

     IF  you  Select and Delete the entire contents of the editor  box,
     the  indicator,  "SELECTING TEXT,"  will still be  displayed, even
     though no currently  selected  text  exists.   Press the space bar
     to create  a  place  for the cursor to go,  and the indicator will
     revert back to ROW: COL:.
  
     CNI  Key  State  indicates  the status of the Capitol Lock, Number
     Lock, and Insert status.  If  the corresponding letter is visible,
     then the state is on.

     ROW: COL:  indicates  the current cursor position, relative to the
     loaded or selected item in the Lower List Box.   It  includes  all
     text of all current Blocks.
  


*    Selecting Files:
     
     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³E:\TEST\                                      ³  Filename Text Box
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
                               [E:                 ]  Drive Box
     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³ 4TEXT.TXT              ³ E:\                  Root
     ³ BHELP.EXE             ² ³  TEST              ²  1st level directory
     ³ BHELP.HLP             ° ³   BLOCKS           °  2nd level directory
     ³ BOB.BAT               ° ³   TEMP             °  2nd level directory
     ³ BOB.TXT               ° ³   MYPPL            °  2nd level directory
     ³ BOBSFRM.TXT            ³    INCSTUFF          3rd level directory
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
            File Box               Directory Box      
                                Each subsequent level        
                             (Shifts right, 1 character)
     
     The Drive, Directory, File objects provide a quick  and  easy  way
     of accessing any file on your system.   Use the  TAB or  SHIFT TAB
     keys to change focus between the boxes.   As each  object receives
     focus, the default or  top  item  in  each  list  is  highlighted, 
     building a complete Path  in the  Filename Text Box.  You may also 
     type directly into the Filename Text Box.

     When the Drive Box has focus,  you  may use the Arrow Keys, or any
     Letter Key to select the drive.  If you choose a floppy drive that
     is not  ready,  you  will  receive  Error Messages. Press Enter to 
     resume.

     Left  Clicking  the  Drive  Box will drop down a full selection of
     available drives to pick from. Left Click an item from this list.

     The File and Directory Boxes function the same as the Active Module
     List Box.  See Active Module List Box

     If  you  press Enter or Double Left Click a highlighted item in the
     Directory List Box,  the  Current Default Directory will be changed
     to that Directory selection. See example below:

      Before                     After pressing Enter on E:\
      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³ E:\                     ³ E:\               Root
      ³  TEST            ²       ³  TEST            ² 1st level directory
      ³   BLOCKS         °       ³  FMN             ° 1st level directory
      ³   TEMP           °       ³  VED             ° 1st level directory
      ³                  °       ³  PCBOARD         ° 1st level directory
      ³                         ³                  
      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

     Key Commands:   ALL KEYS, SHIFT STATES AS DEFINED

     Left, Right, Up, Down Arrow     moves  1   item   in   respective
                                     direction.
     
     Home                            moves to beginning of list.
     End                             moves to end of list.

     Page Up                         moves one list length up. 
     Page Down                       moves one list length down.

     A to Z, or a to z               moves  to  the  item  whose  first
                                     letter matches the pressed key.

                                     Subsequent  presses of a  key  that
                                     matching several items in the list,
                                     will move the selection to the next
                                     matching item in the list.
     
     Tab and Shift + Tab             will set Focus to the next available 
                                     object. Tab orders forward and Shift
                                     + Tab reverse.

     Enter Key                       pressed on an item in the Directory 
                                     List  Box  will  set  the   current 
                                     directory to that item.
     
     Mouse Commands:

     Left Clicking                   an Item selects the Item.

     Left Click & Drag               scrolls List in respective position.

                                     Left clicking and dragging  beyond
                                     the  vertical  boundaries  of  the
                                     list  box  will cause the list box
                                     to  scroll  in   that   respective
                                     direction.   Upon   releasing  the
                                     button, the item that is selected,
                                     will be loaded.
     
     Double Left Click               on an  item in the  Directory List
                                     Box will set the current directory
                                     to that item.


     TEXT                            You may  type a qualified path and
                                     filename directly in  the Filename 
                                     Text Box.
     


*    Use of Undo:

     Undo will change the contents of the Editor Text Box back to  what
     it was prior to the last edit procedure.  These procedures include
     Cut, Copy, Delete, Paste, Search/Change, or if you have typed text.

     Please note that once a new block set loads, the screen  is  saved, 
     or you switch the contents of the editor box  with  another  module
     or subroutine, Undo is updated, and will not  restore  from  a pre-
     vious edit procedure.
     
  

*    Text Manipulation:

     To Select Text in the Editor Text Box:

          1.      Hold down the SHIFT KEY.
          2.      Move the cursor using the arrow keys in the direction
                  desired,  covering  the  text to be selected with the
                  highlighted color.
          3.      Release the keys. The text is now selected.

          Combination keys may also be used, see Key Commands.

          Once text  is selected, it may be erased, clipped and stored,
          duplicated, or added to the clipboard's existing contents.

          The Clipboard is an invisible object which has  the  ability
          to  store  approximately   32,500  characters.  In  many  of
          BOBSLED's  functions  the  ability of the Clipboard is taken
          advantage of.

          For the purpose of Text Editing, consider the Clipboard to be
          a Static Object,  in other words,  what ever is copied to the
          clipboard,  remains  there until it is changed.  This enables 
          you to copy from one project and paste into another.

          When text is being selected, the ROW: COL:  indicator changes
          to SELECTING TEXT, and is displayed in Red, until the text is
          deselected and/or the current cursor position has changed.

          IF you Select and Delete the entire contents of the editor box,
          the indicator, "SELECTING TEXT," will still be displayed, even
          though no currently selected text exists.  Press the space bar
          to create a place for the cursor to go, and the indicator will
          revert back to ROW: COL:.

     Functions:

     Copy         Copies the Selected Text to the Clipboard, replacing
                  its current contents.

     Cut          Removes  the  Selected  Text from the Editor Box and
                  replaces the current  contents of the Clipboard with
                  the Selected Text.

     Delete       Removes the Selected Text from the Editor Box.
     
     Append       Adds the Selected Text to the current contents of the
                  Clipboard.

     Paste        Inserts  the current contents of the Clipboard at the
                  current cursor position.
               
                  Use ^P as a Hot Key for Paste.

                  Note:  Attempting to  use  any of the above functions
                         without first  Selecting  Text,  will  display
                         this Help Screen!

     Key Commands:
     
     Shift + Arrows      selects text in respective direction, selected
                         text becomes highlighted.
                        
     ^Shift + Grey Key   selects  text  and  carries out the grey key's
                         function.

                         For example, SHIFT + CONTROL + END, will select
                         text from the current  cursor  position  to the
                         end of the window.  You  can  not  select  text
                         across multiple block sets.
                        
                         Pressing  an  arrow  key after text is selected
                         will deselect the text.
     
                         If text is selected,  pressing  delete,  or any
                         character key will erase the selected  text, or
                         replace the selected text with that character.

     Mouse Commands:

     Left Clicking Text              sets the cursor position to the mouse
                                     cursor position.

     Left Click & Drag               selects text in respective position.
                                     Left clicking while text is selected
                                     deselects text.

                                     Left clicking and dragging beyond the
                                     vertical  boundaries  of the text box
                                     will cause the text  box to scroll in
                                     that respective direction, while text
                                     is being selected.



*    Time/Date Stamp:

     This function pastes the current CMOS time and date at the current
     cursor position.  If your system does not have a  CMOS chip, or it
     is not compatible with BOBSLED,  the current  DOS time and date is
     used.

     Example Format: 2:04:44 am   April 04, 1994



*    Shelling to the DOS Prompt:

     This function allows full access to DOS,  with  out  using  a vast
     amount  of your low memory.  BOBSLED's  complete  state  and  data
     are  preserved  in  a  file called, "SSHELL.TMP," while you remain
     in the shell. 

     To exit DOS,  and  return to BOBSLED, simply type "EXIT" and press
     Enter.  While you  are  shelled the bottom 2 lines of your display
     screen are locked from scrolling and reflect the "EXIT" message.

     You may execute any program desired while in this shell, including
     a  second  version  of BOBSLED.  Subsequently shelling to DOS from
     BOBSLED, saves the  program  in  a uniquely named file rather than
     overwriting the first shell's  data.  In test runs we were able to
     run multiple copies of BOBSLED  as  well  as Microsoft Windows and
     Desqview,  simultaneously  through  these  shells without crashing
     the system.  Each shell requires about 5K of DOS memory.

     Should  you  occasionally  find strangely named huge files in your
     BOBSLED  directly, and  BOBSLED  is  not  currently  running,  you
     should  delete  them.   When  BOBSLED  returns  from  its shell it
     theoretically deletes the shell file, however from time to time it
     gets missed.

     Many  of  BOBSLED's  functions  run  externally  in similar shells,
     including the HYPER-TEXT HELP, that you are reading.



*    Changing the Object Display Colors:
     
     BOBSLED  allows  you to change your main display  colors to 1 of 4 
     different  preset  combinations.  These  changes mainly affect the 
     Text Editor Box, Active Module List Box, Clipboard Viewer, PPL and 
     PCB Command List Boxes.

     The  color  choices  are  listed in the first prompt box displayed 
     when  calling  this  function.   Press  "OK," then choose a number
     reflecting your choice in the second prompt box.  The color change 
     effect is immediate. Your display color set is stored in BOBSLED's 
     current directory as: "BOBSLED.CFG," so that the  next  time  that 
     you start BOBSLED, your chosen colors will remain active.

     Pressing, or Clicking Cancel aborts the change.



*    Environment Path Setup:

     BOBSLED needs to know the location and names of the executable files 
     for your PPLC.EXE Compiler and PCB Editor.

     Enter the full path and file names including their extensions. Press 
     Enter.  Pressing Cancel aborts the procedure.

     This  information  is  stored  on lines 2 and 3 of the "BOBSLED.CFG" 
     file in your current Directory.
     


*    Shelling to your PCB Editor:

     Before calling this Function, please make sure that you have a PCB 
     Editor, and that its Full Path and Executable Filename,  have been 
     setup in BOBSLED.  To setup this information use the "Environment" 
     function, found under the "Desktop" menu item.

     When calling this function,  you  are  first  prompted to save the 
     files in BOBSLED.  If you haven't, its probably a good practice to 
     do so.  There's always a chance that your system may lock, causing 
     you to reboot, resulting in a partial loss of your work.
     
     No continues, and Cancel aborts the function.        
     
     The second prompt box, asks you to enter any command line switches, 
     or perhaps a file name that you wish to pass to your editor when it 
     opens.  If no parameters are desired, either press Enter, or select 
     Cancel.

     BOBSLED then shells out to your editor.  When you quit your editor 
     program, you will return to BOBSLED in the same state as you left.  
     Running your editor,  from the  environment is useful when you are 
     developing menu prompts in your PPS programs.

     Full Motion  Net  invites you to  try  FMN-EDIT vers. 1.40, a full 
     featured PCB  Editor.   See  the  file "FMNWARE.TXT" included with 
     BOBSLED.



*    Print Function:

     BOBSLED's  Print Function is considerably enhanced over most other
     editor's print utilities. 

     Before calling this function,  you must  either have existing text
     or a file(s) loaded. BOBSLED will not attempt to print, if nothing
     is available to print from.

     Selected text must  be  selected prior to calling this function as
     this form will replace the editor box position while it is visible.


          Ú Print Function ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
          ³                                                  ³
          ³Ú Print Source ÄÄÄÄÄÄÄÄÄ¿Ú Target ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³
          ³³                       ³³                       ³³
          ³³( ) Selected Text      ³³( ) LPT1               ³³
          ³³( ) Clipboard          ³³( ) LPT2               ³³
          ³³() Window             ³³( ) Find port          ³³
          ³³( ) Subroutine         ³³() File               ³³
          ³³( ) Module             ³³                       ³³
          ³³                       ³³[X] Auto Eject         ³³
          ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³
          ³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³
          ³³E:\TEST         ( file input box )              ³³
          ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³
          ³ () Overwrite existing   ( ) Append to existing  ³
          ³                                                  ³
          ³                        ÚÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ³
          ³                        ³   Print  ³ ³   Done   ³ ³
          ³                        ÀÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ³
          ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

          Ú Print Source ÄÄÄÄÄÄÄÄÄ¿ BOBSLED will Print...
          ³                       ³
          ³( ) Selected Text      ³ Any selected text from the editor box.
          ³( ) Clipboard          ³ The current Clipboard contents.
                                    See:  Text Manipulation
        
          ³() Window             ³ The current contents of the editor box.
        
          ³( ) Subroutine         ³ A subroutine from the Lower List box.
          ³( ) Module             ³ An entire Module from the Upper List 
          ³                       ³ box.  See:  Active Module List Box
          ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

          Ú Target ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ BOBSLED will print to...
          ³                       ³
          ³( ) LPT1               ³ Parallel Port 1
          ³( ) LPT2               ³ Parallel Port 2
        
          ³( ) Find port          ³ Finds the correct port, if you are 
                                    not certain.
        
          ³() File               ³ A file that you specify.  Once this
                                    option  is selected, the file input
                                    box will become visible.
          ³                       ³
          ³[X] Auto Eject         ³ If checked,  this option will eject 
          ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ the  printed  page,  when finished.  
                                    If not checked,  some printers will 
                                    retain the output in their buffers, 
                                    rather then  printing and advancing 
                                    to the next page.   Use this option 
                                    primarily to save paper.

          
          ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
          ³E:\TEST         ( file input box )              ³
          ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
           () Overwrite existing   ( ) Append to existing  

     "Overwrite existing,"  replaces the output file where as,  "Append 
     to existing,"  will add the print output to the file.  The default 
     is overwrite.

     Unlike  most  other  print utilities, this function remains Static,
     such once the options  are  chosen  for  any  BOBSLED session, they
     remain set until you quit.  The Print Form will  remain  displayed,
     so that you may select multiple items to print, rather  than having
     to reopen the form 3 times in order to  print 3  subroutines.  When 
     you are through with the print function, simply press Done.  

     BOBSLED will inform you of any print errors.  See: Error Messages
     Should BOBSLED attempt to send more output to your printer  than it 
     can handle,  you will receive a  # 217  Print Error.  Simply, Press 
     "OK,"  and  BOBSLED  will  resume  printing.   An  internal counter
     monitors  various print errors, allowing up to 5 chances for you to 
     correct any external problems, before aborting the print run.
     
     BOBSLED creates  and uses a temporary file,  "TEMP.PRN."  Should you 
     ever find this file in your root directory,  you may delete it.  The 
     Print utility is supposed to delete this file on exit, but sometimes 
     it might be missed.

     Key Commands:   CURSOR KEYS

     Left, Right, Up, Down Arrow     selects buttons of a button set.
                        
                                     Grayed Buttons are not  available.
                                     For example; if you did not select
                                     any  text before calling the print
                                     function,  then  the Selected Text
                                     option will be grayed out.
     
     Tab and Shift + Tab             will  set  Focus   to   the   next 
                                     available set  of buttons or  form 
                                     object.  Tab  orders  forward  and 
                                     Shift + Tab reverse.
     
     Mouse Commands:

     Left Clicking a Button          selects the Button.
     

*    Searching and Changing Text:
     
     BOBSLED provides an extremely versatile function for searching for 
     and changing text.  Like most of BOBSLED's forms, this is a static 
     function.  When re-initiated,  the last values entered will remain 
     displayed.  See:  Repeat a Previous Search/Find

     Before calling this function you must have more than 40 characters
     in the editor box,  or have other  file(s) loaded.  The Search for
     text will begin at the next character following the current cursor
     position.  All Search/Changes are Case Sensitive.

                     Form displayed when Searching for Text
                                           
          Ú  Find Text FunctionÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
          ³                                                           ³
          ³Find:       () Specify  ( ) Clipboard  ( ) Selected Text  ³
          ³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ³
          ³³_                                                       ³ ³
          ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ³
          ³                                                           ³
          ³                                                           ³
          ³                                                           ³
          ³                                                           ³
          ³Ú Search ÄÄÄÄÄÄÄÄÄÄÄÄ¿Ú Begin at ÄÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ³
          ³³( ) Selected Text   ³³                     ³ ³          ³ ³
          ³³() Window          ³³() Top              ³ ³   Find   ³ ³
          ³³( ) Subroutine      ³³( ) Cursor Position  ³ ³          ³ ³
          ³³( ) Module          ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ³
          ³³( ) Global          ³                                     ³
          ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ                        <   Done   > ³
          ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

                        Form displayed when Changing Text
                                           
          Ú Change Text Function ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
          ³                                                           ³
          ³Find:       () Specify  ( ) Clipboard  ( ) Selected Text  ³
          ³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ³
          ³³_                                                       ³ ³
          ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ³
          ³Change to:  () Specify  ( ) Clipboard  ( ) Selected Text  ³
          ³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ³
          ³³_                                                       ³ ³
          ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ³
          ³Ú Search ÄÄÄÄÄÄÄÄÄÄÄÄ¿Ú Begin at ÄÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄ¿ ³
          ³³( ) Selected Text   ³³                     ³ ³          ³ ³
          ³³() Window          ³³() Top              ³ ³  Change  ³ ³
          ³³( ) Subroutine      ³³( ) Cursor Position  ³ ³          ³ ³
          ³³( ) Module          ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÙ ³
          ³³( ) Global          ³                                     ³
          ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ [X] Verify Change      <   Done   > ³
          ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
     
     Button/Box Definition:
     
     Find Box:            Enter  the  text or characters to search for.  
                          You may use extended DOS  characters as well.  
                          See:  Ascii Chart
     
                          Text length is set at 32,500 characters.


     () Specify          If  selected  you must use the Find Box,  see 
                          above.

     ( ) Clipboard        Searches for text matching Clipboard contents.
     ( ) Selected Text    Searches for text matching the Selected Text.

     Change to Box:       Enter the  text  or  characters to change the 
                          found pattern to.  If  blank, will delete the 
                          found text.
     
                          Text length is set at 32,500 characters.
     
     () Specify          If selected you must use Change Box, see above.
     ( ) Clipboard        Replaces found text with the Clipboard contents.
     
        Note:  If the length of the Editor Box Contents plus the contents 
               of the Clipboard,  exceeds  24K,  then  this  function  is 
               aborted, and you will receive a message  indicating  this.  
               This prevents BOBSLED from running out of String Memory.
     
     ( ) Selected Text    Replaces found text with the Selected Text.

     Search:              Where to conduct the search.
     
     ( ) Selected Text    Searches only in the Selected Text.
     () Window           Searches only in the Editor  Window,  or  the 
                          current Block Set, if multiple Blocks make up 
                          the loaded file.
     
     ( ) Subroutine       Searches only the selected Subroutine.
                          See:  Active Sunroutine List Box
                          
     ( ) Module           Searches only the selected Module or Text file.
                          See:  Active Module List Box

     ( ) Global           Searches all loaded files in BOBSLED.
     
     Begin at:            Where to start searching.

     () Top              Starts at the beginning of the Window or First
                          Block Set.  See:  Block Sets

     ( ) Cursor Position  Starts  at the current cursor  position.  Not 
                          available for use with Module, or Global. 

     [X] Verify Change    If changing text, you will:  
                   
                          1.  Hear a signal tone when a match was found.
                          2.  The match will be in view and highlighted.
                          3.  There will be a 1 second pause.
                          4.  You will be then prompted to Change, Skip
                              or Cancel the search. 
                    
                              Prompt = "YES, NO, CANCEL"       

     BOBSLED's  prompt  will  always be displayed  in the center of the 
     screen.  This prevents you from  having  to  "chase"  the  prompt.
     Simply position the Mouse Cursor  over  a  button,  and the prompt
     will appear under your cursor, each time it displays.

     If the Verify  box is  not  checked,  all  changes  are  conducted 
     automatically.
     
     ÚÄÄÄÄÄÄÄÄ¿
     ³ Change ³           Executes function.
     ÀÄÄÄÄÄÄÄÄÙ
     
     <   Done   >         Exits function.


     Grayed Buttons  are  not  available.  For example;  if you did not 
     select  any  text  before  calling  the  print  function, then the 
     Selected Text option will be grayed out.
     
     While  the  Search/Change  Function  is running the current cursor
     position is not updated.  When you end  the  search,  the  correct
     ROW: COL: values will be displayed.
     
     If  no  matches  are  found  you  will  hear a Low Error Tone, and 
     receive a message indicating this.  If there were matches, but the 
     function has reached the end of the search boundary, you will hear 
     a Low Error Tone,  and  the  display  will reset to the top of the 
     file or lower limit of the search boundary.

     As the function  finds matches,  they will be highlighted, and you        
     will  here a prompt tone.  The  Search/Find  function  ends  after
     finding  its  first match, therefore using this function will pro-
     vide a method of continuation,  even if you have  changed files or 
     subroutines.  See:  Active Module List Box

     Key Commands:   CURSOR KEYS

     Left, Right, Up,     selects buttons of a button set.
     Down Arrow     
                          Grayed Buttons are not available. For example 
                          if you did not select any text before calling 
                          this function,  then the Selected Text option 
                          will be grayed out.
     
     Tab & Shift + Tab    will set Focus to the next  available  set of 
                          buttons  or  form  object. Tab orders forward 
                          and Shift + Tab reverse.

     F3                   continues a previous search.  
                          See:  Repeat a Previous Search/Find

                          A  Repeat  Find  can  not  be executed if the 
                          previous initialization was a  Search Change, 
                          or no previous Find parameter was setup.
     
     Mouse Commands:

     Left Clicking        an Item selects the Item.



*    Repeat a Previous Search/Find:

     Restarts or continues from a previous  Search.  This  function can
     not be used if the previous function  was  a  Search/Change,  only
     from a Find.  If one is attempted,  or  no  previous  Search para-
     meters exist, you will hear a Low Error Tone, and receive a  Local 
     Error message.

     If  no  matches  are  found  you  will  hear a Low Error Tone, and 
     receive 
     a message indicating this. If there were matches, but the function
     has  reached  the  end of the search boundary, you will hear a Low 
     Error Tone,  and the  display will reset to the top of the file or 
     lower limit of the search boundary.

     As the function finds matches,  they will be highlighted,  and you        
     will here a prompt tone.   The  Search/Find  function  ends  after
     finding  its  first  match,  therefore  using  this  function will 
     provide a method of continuation, even if you have  changed  files
     or subroutines.  See:  Active Module List Box
     
     You may also use the Hot Key "F3" to access this function.
     
     

*    Sub Manipulation:

     BOBSLED includes various procedures manipulating Subroutines.
     
     Topics covered in this section include:
     
          Creating a New Subroutine
          Renaming a Subroutine
          Re-ordering Subroutines in a Module

          Copy a Subroutine
          Moving a Subroutine
          Removing a Subroutine
     
          Removing a Loaded Module
     

*    Creating a New Subroutine:

          1.      Highlight the Module to add  the new  Subroutine  to.
          2.      Activate  the function from the menu.  You  may  also 
                  use the Hot Key, "Control + S."
          3.      You are then prompted with an input box to  enter the 
                  name that you wish to call the subroutine.
               
                  An existing uniquely named word appears in  this box.  
                  You  may  choose  to  keep  this  name,  or  call the 
                  subroutine something else.

                  Do not include spaces or use an underline as the  8th 
                  letter in the word.  You may have a name  longer than 
                  8  characters,  however when BOBSYS  parses your sub-
                  routines to temporary  files,  it  will  only use the 
                  first 8 characters  of the name.  It will cause prob-
                  lems  if  more  than  2 of  your subroutines have the 
                  same first 8 characters.
          
          4.      Press Enter or Click "OK," to continue, Cancel aborts.

          5.      The new subroutine is added to the end of the list in
                  the  Active Subroutine List Box
               
          6.      The new subroutine will contain the following syntax:

                  SUB Subname

                  END SUB
          
                  ( where Subname is what you called it )

          7.      Be sure and insert the Call Statement to this subrou-
                  tine somewhere  in  your  Module level code,  or from 
                  another subroutine.

                  Syntax:         CALL Subname

                  Do  not  put  any  comments  or  labels on this line, 
                  otherwise you will confuse the Translator. The state-
                  ment Is Case Sensitive.  It's a  good idea  to always 
                  use the same case  structure for duplicate statements 
                  throughout your program.

                  The translator will convert these statements to valid 
                  PPS syntax for you.

     When  BOBSYS finds a duplicate subroutine  name,  the first 8 char-
     acters, it will prompt you to rename the  duplicate subroutine, by 
     replacing  the  8th character with an  underline.  Please  keep in 
     mind  that  this procedure is strictly to keep  track of the temp-
     orary files and in no way affects  the actual  sub name written in 
     the code of your file. The only change that you  will notice is in 
     the  Active  Module/Subroutine  List Box.  Only the  first 8 char- 
     acters of any subroutine appear as list items,  and  all duplicate 
     subs have an  underline.  If you  loaded  any of  these items, you 
     would notice that the  actual code retains the original  name even 
     if it is  a  duplicate.   This method prevents BOBSLED from  over-
     writing subroutines with the same or similar names.

     
*    Renaming a Subroutine:

          1.      To rename a subroutine, simply change the name in the 
                  editor box, make sure you also change any CALL State-
                  ments reflecting the old name.

          2.      Save the Module.

          3.      Reload the Module, using "Open a Project."

          4.      BOBSYS will parse your new subroutine.
                  

*    Re-ordering Subroutines:

          1.      Rename the subroutine using a first letter lower than 
                  the value of any existing subroutines.  For  example, 
                  put the letter, "Z," in front of it.  Make  sure  you 
                  also change any CALL Statements  reflecting  the  old 
                  name.
          
          2.      Save the Module.

          3.      Reload the Module, using "Open a Project."

          4.      BOBSYS will parse your subroutines using the new order.  
                  BOBSLED loads and  saves  your  subroutines in alphabe-
                  tical order when rebuilding Modules.


*    Copy a Subroutine:

          1.      BOBSLED  will not allow you to Copy a Subroutine to a 
                  Text file.  
               
          2.      If only one Module is loaded,  attempting to activate 
                  this function will generate a Low Error Tone.  
               
                  Your  loaded Modules must also be saved as a Project, 
                  prior to using this function.

                  See:  Saving a Project

          
          3.      You must select the Subroutine to Copy before calling 
                  this function.

          4.      Highlight or Select the Subroutine to Copy.

          5.      If  more  than two Modules are loaded, but you choose 
                  to Copy the  Subroutine  to  the  same Module, BOBSYS 
                  will prompt  you  to  rename  its  temporary file for 
                  your  subroutine,  using  an  underline  as  its  8th 
                  character.

                  See: Creating a New Subroutine, last paragraph.
                  
          6.      Enter the  name  of  the Module to Copy to.  You must 
                  type in the full filename and extension, that appears 
                  in the Active Module List Box. This entry is not case 
                  sensitive. If you can not remember what the Module is 
                  called, and the Input  Box  is  blocking  your  view, 
                  simply drag the Box by its top corner somewhere  else, 
                  using the Mouse.

          7.      Press Enter, or select "OK," Cancel aborts.

          8.      BOBSYS will reparse and reload.

          9.      Do not attempt to Copy a previously Copied Subroutine, 
                  "one already with an underline as the  8th character."  
                  This  will  most likely result in overwriting the sub-
                  routine.  Rename the subroutine and reload the Module, 
                  first.   

                  See:  Renaming a Subroutine
                  

*    Moving a Subroutine:

          1.      BOBSLED will not allow you to Move a  Subroutine to a 
                  Text file.  
               
          2.      If only one Module is loaded,  attempting to activate 
                  this function will generate a Low Error Tone.  
               
          3.      You must select the Subroutine to Move before calling 
                  this function.

          4.      Highlight or Select the Subroutine to Move.

          5.      If more  than two  Modules are loaded, but you choose 
                  to Move the Subroutine  to  the same Module, the only 
                  thing that you will achieve is to re-order the Active 
                  List Box.  Once BOBSYS reparses your Module, the pre-
                  vious order will return.  
               
                  See:  Re-ordering Subroutines

          6.      Enter the  name  of  th e Module to Move to. You must 
                  type in the full filename and extension, that appears 
                  in the Active Module List Box. This entry is not case 
                  sensitive. If you can not remember what the Module is 
                  called, and the Input  Box  is  blocking  your  view, 
                  simply drag the Box by its top corner somewhere else, 
                  using the Mouse.

          7.      Press Enter, or select "OK," Cancel aborts.

          8.      BOBSYS will reparse and reload.
     

*    Removing a Subroutine:
          
          1.      Select the Subroutine to Remove.
          2.      Activate the function from the menu.
          3.      Select Yes or No to save.
          4.      Prompt verifies your selection.
          5.      Press "OK" or Enter to continue, Cancel aborts.
          6.      BOBSYS will reparse and reload.

          Attempting to remove an unselected Subroutine will generate 
          an error message.
          

*    Removing a Loaded Module:

          1.      Select the Module to Remove.
          2.      Activate the function from the menu.
          3.      Select Yes or No to save.
          4.      Prompt verifies your selection.
          5.      Press "OK" or Enter to continue, Cancel aborts.
          6.      BOBSYS will reparse and reload.


          Attempting  to remove an unselected  Module will  generate an 
          error message.



*    Using the File Load/Save Object:

     BOBSLED  uses  the  same  form to handle  each  of  the  following 
     functions.
     
     
          Creating/Opening a New Module
          
          Adding a Module
          Opening a New Module
          Opening a Project File
          
          Save As
          Saving a Module
          Saving a Project
     
     Form used for all procedures,  only  the Header will change.  Some 
     Option Buttons may be Grayed, according to the procedure.
          
     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ 
     ³              Open a new project...    ( Header ) ³  The Headers will
     ³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³  change according
     ³³E:\TEST\                                        ³³  to each specific
     ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³  function called.
     ³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿[E:                    ]³ 
     ³³ 4TEXT.TXT             ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³ 
     ³³ BHELP.EXE             ²³ E:\                   ³ 
     ³³ BHELP.HLP             °³  TEST                  ³ 
     ³³ BOB.BAT               °³   BLOCKS              °³ 
     ³³ BOB.TXT               °³   TEMP                °³ 
     ³³ BOBSFRM.TXT           ³                       ³ 
     ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³ 
     ³Ú File Pattern Spec ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ÚÄÄÄÄÄÄÄÄÄÄ¿³ 
     ³³                                    ³³   Open   ³³ 
     ³³( ) 1 *.PRJ ( ) 2 *.BPS ( ) 3 *.TXT ³ÀÄÄÄÄÄÄÄÄÄÄÙ³ 
     ³³                                    ³ÚÄÄÄÄÄÄÄÄÄÄ¿³ 
     ³³    () 4 Specify [*.*         ]    ³³   Done   ³³ 
     ³ÀÄÄOption ButtonsÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙÀÄÄÄÄÄÄÄÄÄÄÙ³ 
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ 

     The  File Pattern Spec Buttons,  affect the files in the File Box.
     If you  Select Button 1,  only those files having a  PRJ extension 
     will be displayed.

     Button 4,  allows you to specify  the filespec to search for.  You 
     may use wild card characters, as well as a specific filename.

     Once Button 4 is selected, press the right arrow key to get to the 
     spec box.  After entering the spec,  either press TAB or ENTER, to 
     move  to  the  OPEN  button.   You may use the Mouse to make these 
     selections directly.
     
     Key Commands/Functions:   CURSOR KEYS

     Left, Right, Up,     selects buttons of a button set.
     Down Arrow                   
                          Grayed Buttons are not available. For example 
                          if you  are  Adding  a  Module,  the  Project 
                          option will be Grayed, and unavailable.
     
     Tab & Shift + Tab    will set Focus to the next available  set  of 
                          buttons or form object.  Tab  orders  forward 
                          and Shift + Tab reverse.
     
     ( ) 4 Specify [*.*]  Select, type spec, press Enter or right arrow, 
                          to move to Open Button.

                          Wildcard  examples  include:   ?,  *,  name.*, 
                          *.ext, n??e.*, ETC. Do not include the commas.

                          Once focus leaves the filespec box,  the file 
                          pattern will be updated.
                        
     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿   You may enter a filename  directly into  this
     ³E:\TEST\        ³   box.  You must supply  its  extension.  If it 
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ   has no extension, it can not be loaded.
     ( File Text Box )    
     
     Drive, Directory,    See:  Selecting Files
     File Box


     F2                   Saving a Project, Hot Key
     
     Mouse Commands:

     Left Clicking        an Item selects the Item.
          
*    Creating/Opening a New Module:
               
          1.      Select "New Module" from the menu.
          2.      Enter the name that you  desire in the  File Text Box, 
                  make sure it includes a BPS extension.  See: Selecting

          3.      Select Open.
          4.      When BOBSYS, asks you if you want to create  the file, 
                  select YES.

          5.      Your new Module will contain the 3 following lines:

                        ;Module Name
                        ;Date   Time
                        ;
     
                  Modular Name is the filename that you specified.
     

*    Adding a Module:
     
          1.      Select "Add Module" from the menu.
          2.      Select the file to load. See: Selecting
          3.      Press "Add."
          4.      You may continue to add additional files  or  Press,
                  "Done," to close the function box.

          5.      BOBSLED will allow you to add up to 32,500 files.
            

*    Opening a Project File:

          1.      Select "Open Project" from the menu.
          2.      Select the Project File to  load.  You may also load 
                  other files instead of a Project File. 
          
          3.      Press "Open."
          4.      Press "Done," to close the function box.
     

*    Saving a Module:
     
          1.      Highlight  or  select  the Module to save from Active 
                  List Box.

          2.      Select "Save Module" 
          

*    Save As:
     
          1.      Highlight or select the Module, or file to Save as, or 
                  if this is new work and no other files are loaded,  go 
                  to step 2.
          
          2.      Select the filename to save as.  See: Selecting
          
          3.      Select "Save" 
                  
     
*    Saving a Project:

          If the Project already exists,  BOBSLED will only rebuild and 
          save your files, updating where necessary.

          If  your  work was not previously saved as a Project, BOBSLED
          will  prompt you for a Project Name.  Enter the desired name,
          specifying the  ".PRJ"  extension. Press Enter or select "OK"
          to continue, or select Cancel to abort the procedure.
          
          

*Translating a Source File:

 Translate will convert a BPS source file into a valid PPS source file.
 
 Ú´                                BOBSLED                                Ã¿
 ³ ð  File  Edit  Search  Tools  Run  Desktop  F1ùHelp [ PP.BPS Startup ]  ³
 ³Ú Custom Translator Interface ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³
 ³³                                                  ³³   Active Module   ³³
 ³³Select the Module or Item from the top List Box.  ³³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³³
 ³³Select the type of source file to make PPS or INC.³³³ PP.BPS          ³³
 ³³Modify the Target, if desired.  Press Translate.  ³³³                 ²³³
 ³³                                                  ³³³                 °³³
 ³³Source: Active Module                             ³³³                 ³³
 ³³PP.BPS                                            ³³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³³
 ³³                                                  ³³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³³
 ³³Target: Specified                                 ³³³ PP.BPS          ³³
 ³³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³³³                 ²³³
 ³³³E:\TEST\PP.PPS                                  ³³³³                 °³³
 ³³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³³³                 °³³
 ³³Ú Target File Type ÄÄÄÄÄ¿          ÚÄÄÄÄÄÄÄÄÄÄÄ¿  ³³³                 °³³
 ³³³                       ³          ³ Translate ³  ³³³                 °³³
 ³³³() PPS File           ³          ÀÄÄÄÄÄÄÄÄÄÄÄÙ  ³³³                 °³³
 ³³³                       ³          ÚÄÄÄÄÄÄÄÄÄÄÄ¿  ³³³                 °³³
 ³³³( ) INC File           ³          ³    Done   ³  ³³³                 ³³
 ³³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ          ÀÄÄÄÄÄÄÄÄÄÄÄÙ  ³³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³³
 ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³
 ³                                                 Block 0 of 0 Free: 32435³
 ³  Ctrl-E Min   Blanker   Line Draw    Goto Block  ROW: 2 COL: 33       I ³
 ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
                       (form shown smaller than actual size)    
     
     Procedure:

     1.   You will first be prompted to save your work. If you made any 
          recent changes, that you wish to be included in your Transla-
          tion, you should Save, Now!
     
     2.   If your files are saved as a Project, then upon executing this 
          function, you will be given a choice of either letting BOBSLED 
          conduct  an  Automatic  Translate, or allowing you to manually 
          select the files to be Translated.

          If your files are not saved as a Project, you must make manual 
          choices from the above form.

*         Automatic Translate:

          1.      BOBSLED will create a directory based on your Project 
                  Filename, off the current directory.

                  "MYPPL.PRJ" will become "\MYPPL"

          2.      Your Top or Startup Module the first Module listed in 
                  the Active  Module Box,  will be  translated to a PPS 
                  source file, saved  with  a ".PPS"  extension, in the 
                  newly created directory.

          3.      Any subsequent  Modules  in the top list box, will be 
                  also translated, but saved with an, ".INC" extension.  
                  INC files are considered  Include  files,  externally 
                  called routines from within a PPS source file.
         
*         If you choose to manually translate your files, then this is 
          the following procedure:

          1.  Focus is  set  to  the Active Module List Box. Select the 
              desired Module to Translate.    

          2.  Select  the  type of file to generate, either,  "PPS"  or 
              "INC".

          3.  Make sure the target,  destination  of  the  file  to  be
              translated is correct.

          4.  Select Translate.    
          
          5.  When you are finished translating all the files  desired,
              select Done.

     3.   Your original "BPS" file, will not be affected  by Translate, 
          so  that  you  may  at  any time reload this file for further 
          editing.

     Key Commands:   CURSOR KEYS

     
     Left, Right, Up,     selects buttons of a button set.
     Down Arrow                   
     
     Tab & Shift + Tab    will set Focus to the next available set of 
                          buttons or form object.  Tab orders forward 
                          and Shift + Tab reverse.

     F10                  is the Hot Key to call this function.

     Mouse Commands:

     Left Clicking        an Item selects the Item.
     
     

* Compiling a Source File:
 
  BOBSLED executes the PPE Compiler, "PPLC.EXE" from within its environ-
  ment, and provides a method to view any compiler warnings or messages, 
  in a timed shell.  "PPLC.EXE"  is not provided with BOBSLED, you must 
  obtain this file from Clark Development Co., Inc.


  Ú´                                BOBSLED                              Ã¿
  ³  ð  File  Edit  Search  Tools  Run  Desktop  F1ùHelp  [ NONE ]        ³
  ³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³
  ³³              Compile a PPS file...          ³ ³     Active Module   ³³
  ³³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³ ³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³³
  ³³³E:\TEST\                                   ³³ ³³ Untitled          ³³
  ³³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³ ³³                   ²³³
  ³³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿[E:               ]³ ³³                   °³³
  ³³³ MYPPL.PPS             ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³ ³³                   ³³
  ³³³                       ²³ E:\              ³ ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³³
  ³³³                       °³  TEST            ²³ ³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³³
  ³³³                       °³   BLOCKS         °³ ³³                   ³³
  ³³³                       °³   TEMP           °³ ³³                   ²³³
  ³³³                       ³                  ³ ³³                   °³³
  ³³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³ ³³                   °³³
  ³³                                    ÚÄÄÄÄÄÄÄ¿³ ³³                   °³³
  ³³Ú File Pattern Spec ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³Compile³³ ³³                   °³³
  ³³³( ) 1 *.PRJ( ) 2 *.BPS( ) 3 *.TXT ³ÀÄÄÄÄÄÄÄÙ³ ³³                   °³³
  ³³³                                  ³ÚÄÄÄÄÄÄÄ¿³ ³³                   °³³
  ³³³    () 4 Specify [*.PPS       ]  ³³ Done  ³³ ³³                   ³³
  ³³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙÀÄÄÄÄÄÄÄÙ³ ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³³
  ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³
  ³                                                            Free: 32500³
  ³ Ctrl-E Min   Blanker   Line Draw   Goto Block   ROW: 1 COL: 1       I ³
  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
                      (form shown smaller than actual size)
  
  Before  attempting  to  Compile a source file, please make sure you have
  setup the Compiler Path. See:  Environment Path Setup
     
     Procedure:

     1.   Select to save your files at the first prompt.  "YES"  saves,
          "NO" continues without saving, "Cancel" aborts this function.

     2.   Enter any Compiler Switches.  See:  Compiling a PPE

     3.   When the Compile Form appears, select the file to Compile.

     4.   Select Compile.

     5.   PPLC.EXE  will  compile  your selected  source file using the 
          command line switches specified, if any.  You will be able to 
          view any warnings or errors.

          After  compilation,  the  DOS shell will remain open for your 
          use,  for a timed period.   You may run any other programs or 
          execute any function from within this shell. As long as some-
          thing is running, you are pressing keys, the timer will reset.  
          Left unattended, BOBSLED will return in  90  seconds,  or you 
          may type EXIT and Press Enter, to return immediately.

     6.   Select Done to close the form.

     Key Commands:   CURSOR KEYS

     Left, Right, Up,     selects buttons of a button set.
     Down Arrow     
          
     Tab & Shift + Tab    will  set Focus to the next  available set of 
                          buttons  or  form object.  Tab orders forward 
                          and Shift + Tab reverse.

     F11                  is the Hot Key to call this function.

     Mouse Commands:

     Left Clicking        an Item selects the Item.
     


* Running a PPE from BOBSLED:

  BOBSLED  provides a method for you to Run your PPE executable file in 
  PC Board, from its environment.

  You  must  have  a Usable Node on PC Board, the PPE.PPE file which is 
  included with BOBSLED, and have already setup the required parameters 
  as according to  "BOBSRUN.DOC" which  is also included in the BOBSLED 
  package. "BOBSRUN.DOC" instructs you on the usage of BOBSRUN.BAT  and 
  other related topics.
  
  Ú´                                BOBSLED                              Ã¿
  ³  ð  File  Edit  Search  Tools  Run  Desktop  F1ùHelp  [ NONE ]        ³
  ³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³
  ³³            Run a PPE in PC Board...         ³ ³     Active Module   ³³
  ³³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³ ³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³³
  ³³³E:\TEST\                                   ³³ ³³ Untitled          ³³
  ³³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³ ³³                   ²³³
  ³³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿[E:               ]³ ³³                   °³³
  ³³³ MYPPL.PPE             ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³ ³³                   ³³
  ³³³                       ²³ E:\              ³ ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³³
  ³³³                       °³  TEST            ²³ ³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³³
  ³³³                       °³   BLOCKS         °³ ³³                   ³³
  ³³³                       °³   TEMP           °³ ³³                   ²³³
  ³³³                       ³                  ³ ³³                   °³³
  ³³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³ ³³                   °³³
  ³³Ú File Pattern Spec ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ÚÄÄÄÄÄÄÄ¿³ ³³                   °³³
  ³³³                                  ³³Run PPE³³ ³³                   °³³
  ³³³( ) 1 *.PRJ( ) 2 *.BPS( ) 3 *.TXT ³ÀÄÄÄÄÄÄÄÙ³ ³³                   °³³
  ³³³                                  ³ÚÄÄÄÄÄÄÄ¿³ ³³                   °³³
  ³³³    () 4 Specify [*.PPE       ]  ³³ Done  ³³ ³³                   ³³
  ³³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙÀÄÄÄÄÄÄÄÙ³ ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³³
  ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³
  ³                                                            Free: 32500³
  ³ Ctrl-E Min   Blanker   Line Draw   Goto Block   ROW: 1 COL: 1       I ³
  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
                     (form shown smaller than actual size)
     
     Procedure:

     1.   Select to save your files at the first prompt.  "YES"  saves,
          "NO" continues without saving, "Cancel" aborts this function.

     2.   Enter any Parameters or Switches.  See:  Run PPE

     3.   When the Run Form appears, select the file to Run.

     4.   Select RUN PPE

     5.   Your PPE will then be executed in PC Board.  When you exit PC 
          Board you will return to BOBSLED.

     6.   Select Done to close the form.
          
     Key Commands:   CURSOR KEYS
          
     Left, Right, Up,     selects buttons of a button set.
     Down Arrow     
     
     Tab & Shift + Tab    will  set Focus to the next  available set of 
                          buttons  or form object.  Tab  orders forward 
                          and Shift + Tab reverse.

     F12                  is the Hot Key to call this function.

     Mouse Commands:

     Left Clicking        an Item selects the Item.

     


*    PCB & PPL Command List Box:

     BOBSLED provides quick access to PPL Command Statements, as well as
     PCB @Macro Commands, using a End User adjustable List Box.  You  as
     the developer, can Add, Remove, or Modify any Item in the Lists, to
     suit your programming tastes!


     Ú´                                  BOBSLED                         Ã¿
     ³  ð  File  Edit  Search  Tools  Run  Desktop  F1ùHelp  [ NONE ]     ³
     ³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³
     ³³                                                                  ³
     ³³                                                                  ²³
     ³³                                                                  °³
     ³³                                                                  °³
     ³³                                                                  °³
     ³³                                                                  °³
     ³³                                                                  °³
     ³³                                                                  °³
     ³³                                                                  ³
     ³À<°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°>Ù³
     ³Ú PPL Commands ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³
     ³³       < Add Item >   < Remove Item >   < Paste Item >   < Done > ³³
     ³³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³³
     ³³³ ;INCLUDE:FILESPEC.EXT         (compiler directive)             ³³
     ³³³ ABORT()                       (function)                       ²³³
     ³³³ ABS(iexp)                     (function)                       °³³
     ³³³ ADJBYTES bytes                (statement)                      ³³
     ³³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³³
     ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³
     ³                                                         Free: 32500³
     ³ Ctrl-E Max  Blanker  Line Draw   Goto Block  ROW: 1 COL: 1       I ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
                        (form shown smaller than actual size)

     When activated, this function will widen the width of the Editor Box,
     while shortening its height, allowing you to view both the PCB or PPL 
     Command Box at the same time.

     In this way you can transfer Commands both to and from the boxes, very
     quickly. Should you find particular statements that you use frequently,
     you  may  add  these  statements  to your Command List Box, Modify the
     existing ones to suit your needs.
     
     You may also manually add or modify any statement in the "PPLCMDS.DAT"
     or "PCBCMDS.DAT" files, by using the following directive.
          
       PCB Commands Directive:      

       Column 1 >ÄÄ¿      Column 22 >ÄÄÄ¿                 Column 76 >ÄÄÄ¿
                ³                       ³                               ³
                @ALIAS@                 (users alias name)              ³
                @BEEP@                  (sounds beep at remote terminal)³
                ³                       ³                               ³
                Statement               Comment                         EOL
      
       
       PPL Commands Directive:      

       Column 1 >ÄÄ¿      Column 42 >ÄÄÄ¿                 Column 76 >ÄÄÄ¿
                   ³                    ³                               ³
                   @ALIAS@              (users alias name)              ³
                   @BEEP@               (sounds beep at remote terminal)³
                   ³                    ³                               ³
                   Statement            Comment                         EOL
          
          BOBSLED   only   considers  the  first  20 characters  in  the 
          "PCBCMDS.DAT"  file,  and  the  first  40  characters  in  the 
          "PPLCMDS.DAT" file.  The balance  of the line is  reserved for 
          comments.  Please keep in mind that only the  first  76  char-
          acters are ever visible in  BOBSLED.  In our  actual files and 
          in this example we add an extra  space  at  the  41st  column, 
          just for cosmetic reasons.  EOL = "End Of Line"

     Key Commands/Functions:   CURSOR KEYS
     
     Left, Right, Up,     selects buttons of a button set.
     Down Arrow     
     
     Tab & Shift + Tab    will set Focus to the next  available  set of 
                          buttons or form object.  Tab  orders  forward 
                          and Shift + Tab reverse.

     F4                   is the Hot Key for PPL Command List   
     F5                   is the Hot Key for PCB Macro List

     Shift + Arrow Keys   will select text.
     
     < Add Item >         Adds selected text to List Box, if no text is 
                          selected, then you will be prompted  with  an 
                          Input Box, to Enter the Text to be Added.  If 
                          you select or enter text  exceeding  76 char-
                          acters  in  length,  you  will  receive a Low 
                          Error Tone.
     
     < Remove Item >      Deletes highlighted item in List Box.
     
     < Paste Item >       Inserts the highlighted item in  the List Box 
                          at the current cursor position in the  Editor 
                          Text Box.
     
     < Done >             Ends function, saves contents of List Box, to 
                          its proper file, closes box.

     Ctrl-E Max           Toggles Editor screen width.
                          See:  Changing the Editor Screen Width

     Mouse Commands:

     Left Clicking        an Item selects the Item.



*   Clipboard Viewer:

    BOBSLED allows you to physically view and affect the Clipboard  for
    the Editor Text Box.  In this way, you may exploit  its ability for
    holding and swapping text.
    
    Ú´                            BOBSLED                               Ã¿
    ³  ð  File  Edit  Search  Tools  Run  Desktop  F1ùHelp  [ NONE ]     ³
    ³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³
    ³³                                                                  ³
    ³³                                                                  ²³
    ³³                                                                  °³
    ³³                                                                  °³
    ³³                                                                  °³
    ³³                                                                  °³
    ³³                                                                  °³
    ³³                                                                  °³
    ³³                                                                  ³
    ³À <°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°>Ù³
    ³Ú Clipboard Contents ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³
    ³³     <Replace with Active Text>  <Clear contents>  <Close Window> ³³
    ³³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³³
    ³³³                                                                ³³
    ³³³                                                                ²³³
    ³³³                                                                °³³
    ³³³                                                                ³³
    ³³À<²°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°>Ù³³
    ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³
    ³                                                         Free: 32500³
    ³ Ctrl-E Max  Blanker  Line Draw   Goto Block  ROW: 1 COL: 1       I ³
    ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
                    (form shown smaller than actual size)

     When activated, this function will widen the width of the Editor Box,
     while shortening its height, allowing you to view both the  Clipboard
     and the Editor Text Box, at the same time.

     In  this way you can transfer statements, both to and from the boxes, 
     very quickly.  Should you find particular  statements  that  you  use 
     frequently, between Subroutines or Modules,  you  will  benefit  with 
     the use of this "visual clipboard swapper."

     For use with the Syntax Check you must Clear the  contents  of  the
     Clipboard prior to its use.  This prevents BOBSLED  from  overwriting
     any important text you are storing there.
     
     The Clipboard is a temporary storage container.  If  you  would  like
     to save its contents to disk, you may do this using the Print
     Function.  See:  Print Function

     The Clipboard will hold up to 32,500 characters.
     
     Key Commands/Functions:   CURSOR KEYS
     
     Left, Right, Up,     selects buttons of a button set.
     Down Arrow     
     
     Tab & Shift + Tab    will  set Focus to the next available set of 
                          buttons  or form object.  Tab orders forward 
                          and Shift + Tab reverse.

     F7                   is the Hot Key for this function.
     
     Shift + Arrow Keys   will select text.
          
     <Replace with        Overwrites the current Clipboard contents with
      Active Text>        the  currently  selected  text.  If no text is 
                          selected, the Editor Text Window contents will 
                          be used.  See: Changing Block Sets
          
     <Clear contents>     Deletes the current contents of the Clipboard.
     
     <Close Window>       Closes Clipboard Box.
     
     Ctrl-E Max           Toggles Editor screen width.
                          See:  Changing the Editor Screen Width

     Mouse Commands:

     Left Clicking        an Item selects the Item.

     

*    Syntax Check:

     BOBSLED provides you with a method to check for syntactical errors
     that you may have in your Subroutine or Module.   Although this is
     not a complete error checking  utility,  it  does  catch  the most
     common mistakes.

     Before using this function,  you  must  clear the contents of your
     Clipboard.  See:  Clipboard Viewer
     
     This function will output its error text, if any to the Clipboard.

     Procedure:

     1.   Highlight or select an item from the Lower List Box.  
          See:  Active Subroutine List Box
     
     2.   Select function from menu.

     3.   Note messages, when complete.
        
     Possible Syntax Function Error Messages:
     
     Please note that these are not all possible errors, only what this 
     function searches for. 
          
          ERROR = "Missing (Next, End If, or End While) Statement."

          CASE "!=", "<>", "><", "=<", "<="
          CASE "&&", "||", "==", "**", "=>", ">="
          CASE "&", "|", "!", "=", "-", "*"
          CASE "^", "/", "%", "+", "<", ">"
          ERROR = "Can't end line with operator."

          CASE "FOR", "IF", "ELSEIF", "DO WHILE", "WHILE"
          ERROR = "Conditional Expression missing."
          
          ERROR = "Label missing."
          ERROR = "Label must be Left Justified."
          ERROR = "Line Length exceeds compiler parameters."
          ERROR = "Possible Parameter Mismatch."
          ERROR = "Quotation Count Mismatch."
          ERROR = "[]{}() Count Mismatch."
          ERROR = "Label or Comment not recognized"
          ERROR = "File Spec missing after Include statement."
          ERROR = "Can not have a Blank First Line."

          ERROR = "Translation Warning, Comment on CALL Line."
            ³
            ÀÄÄ>  This  is  the  only parameter that BOBSLED  requires, 
                  that  differs  from  the  PPL  Language,  other  than 
                  using Subroutines.

                  If you put a Comment on a Call Line, during Translate, 
                  BOBSLED will produce an erroneous GOSUB statement.
                  
          All listed errors will include the suspected  row and column 
          numbers found at.  In this way, when viewing the  Clipboard, 
          you  may  scroll  down  each  box and compare the error text 
          directly to your source code.
     
     Key Commands:
     
     F9                              is the Hot Key for this function.
     
     All Other Commands              See:  Clipboard Viewer   
     
     

*    Help on Help:
     
     Form Summary:    ( example only partial and compressed )
     
     Current Item        All Topics      "A" Index  Last Topic Item
     ³                   ³                   ³         ³
     ÀÄÄ>B INDEX       ÀÄÄ>Contents      Index   Back
     ÚÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄÂÄ¿ 
     ³A³B³C³D³E³F³G³H³I³J³K³L³M³N³O³P³Q³R³S³T³U³V³W³X³Y³Z³ Selectable
     ÀÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÁÄÙ   Index
        ÀÄÄ> B Index, B is highlighted

     B2W()              BACKUP                  BELL
     BIGSTR             BITCLEAR                BITSET
     BLT                BOOLEAN                 BREAK
     BROADCAST          BYE                     BYTE

                      ÷0A( Hyper Links )
     
     F1 = Help on Screenword       scans  text  at cursor  position for
                                   possible help text

     F2 = Command Box              utility for copping help text

     F10 = Help on Help            displays this topic  
     
     ESC = Quits                   returns to BOBSLED
     
     Current Item:                 Indicates current topic, non-selectable.
     Contents:                     Selectable, displays main topic areas.
     Index:                        Selectable, displays top or "A" Index.
     Back:                         Selectable, displays last topic.  
                   
     All topics are  stored in a stack, last topic is popped off,  thus 
     "last direction" will work only in reverse.

     Selectable Index              Select any Index by pressing Enter or Left
                                   Clicking on a Letter.
     
     Key Commands/Functions:   CURSOR KEYS
     
     Left, Right, Up,              moves 1 space in respective direction.
     Down Arrow     

     ^Left or Right Arrow          moves 1 word in respective direction.

     Home                          moves to beginning of row.
     Control + Home                moves to beginning of help text.
     
     End                           moves to end of row.
     Control + End                 moves to end of help text.
     
     Page Up                       moves one screen up. 
     Page Down                     moves one screen down.
     
     Backspace                     same function as Left Arrow.

     Enter on Hyper Link           accesses  the  Help  Topic  for  the 
                                   Hyper Link.
     
     TAB                           moves right, to next Hyper Link.
     
     A-Z, a-z (letter keys)        moves to next text word  containing
                                   the  upper  case  equivalent of the
                                   letter that was pressed.
     
     F1                            displays Help on  word  at  current
                                   cursor position, if available.

                                   If no Help Topic is available, a red 
                                   message  on  bottom  of  screen will 
                                   indicate this.
     
     F2                            displays Command Utility Box.

     
     F3                            Hot Key for "Contents."
     
     F4                            Hot Key for "Index."
     
     F5                            Hot Key for "Back."
     
     F6                            Hot Key for "WIZTIPS." 
                                   
                                   WIZTIPS will  display  more  detailed
                                   help on the  current  topic,  or pro-
                                   vide  additional   working   examples
                                   that you may copy to your program.

                                   "WIZTIPS" function is only  available
                                   to registered users of  BOBSLED.  The
                                   latest WIZTIP files may be downloaded
                                   from Full Motion Net.  
                                   
                                   See:  FMN Technical Support

     F10 "HELP ON HELP"            displays this topic.
     
     Escape                        returns to BOBSLED.

     ENTER "Gets Hyper Link"       on Hyper Link will return  topic,  on
                                   selectable item will access function.
              
*    Help Function Utility         copies current topic to an editor box 
                                   for capture.

          Copy Active Text         copies selected text, if selected or 
                                   entire contents of window if not, to 
                                   Clipboard.

                                   If there is  existing  text  in  the 
                                   Clipboard,  this  function  will ap-
                                   pend  new  text  to  the  Clipboard, 
                                   rather  than   replacing  it.   This 
                                   prevents you from  having to go back 
                                   and forth, from Help to BOBSLED, you 
                                   can "get it all" in one shot.

          Clear Clipboard          deletes current contents in Clipboard.

          Print Active Text        prints selected text,  if selected or 
                                   entire contents of window  if not, to 
                                   first ready port found. (LPT1 - LPT4)
          
          Close  or "ESC Key"      ends utility function, returns to pre-
                                   vious Help screen.
          
          Shift + Arrow Keys       to Select Text.
     
     Mouse Commands:

     Left Clicking Text            sets the cursor position to the mouse
                                   cursor position.

     Right Clicking Item           selects the item.
     
     
     
*    Local Message Area:

     BOBSLED often performs an enormous amount of procedures during the
     processing of its functions, often with a notable time lag. (1 - 2
     seconds)  During  processing,  you will often notice numerous mes-
     sages in  the  Local  Message  Area.  These messages will keep you 
     informed of what BOBSLED is doing.  See:  Status / Message Areas

     The following are most, if not all, of the messages and some brief 
     definitions.

     Rebuilding Blocks...                   Building a temporary file.
     Processing files...                    Saving a temporary file.
     Search/Change canceled...              User aborted function.
     Translating...
     Loading next block...                  Getting next window.
     Saving block...
     Status:  + Drive not ready             Floppy drive wasn't ready.
     
     Storing and parsing file...
     Processing...
     Updating...
     Syntax Processing...

     No previous initialization found.       
     Can't repeat find from a previous change call.
     
     Please specify the Item!
     Status:  Directory changed to:  "Directory Name"
     
     There is nothing to save...            No  files  are loaded, no text
                                            exists.
     
     Save state is OK...                    Sometimes saving isn't necessary
                                            if  your  work  hasn't  changed,
                                            since the previous save.

     Saving Project...
     Saving Files...
     Nothing was Saved!                     User aborted Saving Function,
                            
                                            BOBSLED was unable to perform
                                            the function.
     
     Some of these messages require you to change the cursor position be-
     fore they turn off.
     
     

*    Error Set:

     Rather than include an enormous document, describing every possible
     known error that can happen in your system, from any known  source,
     here is the basic summary set of  DOS related Errors,  that we used
     when writing BOBSLED.

     The error numbers are valid through DOS 5.0. Critical Errors are in 
     the range of 1-255 while non-critical  errors have 256 added to the 
     actual DOS error number. Therefore,  to  determine DOS non-critical 
     error numbers, subtract 256 from the value returned.
 
          01 = Unknown unit
          02 = Drive/device not ready
          03 = Unknown command
          04 = Data error (CRC)
          05 = Bad request structure length
          06 = Seek error
          07 = Unknown media type
          08 = Sector not found
          09 = Printer out of paper
          10 = Write fault
          11 = Read fault
          12 = General failure
          15 = Invalid disk change
         255 = Attempt to write on write-protected disk (Actually DOS
               error 00)
 
     DOS Non-Critical Error Codes:
 
          01 = Invalid function number
          02 = File not found
          03 = Path not found
          04 = Too many files - no handles left
          05 = Access denied
          06 = Invalid handle
          07 = Memory control blocks destroyed
          08 = Insufficient memory
          09 = Invalid memory block address
          10 = Invalid environment
          11 = Invalid format
          12 = Invalid access code
          13 = Invalid data
          15 = Invalid drive
          16 = Attempt to remove current directory
          17 = Not same device
          18 = No more files
          19 = Disk write protected
          20 = Unknown unit
          21 = Drive not ready
          22 = Unknown command
          23 = Data error (CRC)
          24 = Bad request structure length
          25 = Seek error
          26 = Unknown media type
          27 = Sector not found
          28 = Printer out of paper
          29 = Write fault
          30 = Read fault
          31 = General failure
          32 = Sharing violation
          33 = Lock violation
          34 = Invalid disk change
          35 = FCB unavailable
          36 = Sharing buffer overflow
          50 = Network request not supported
          51 = Remote computer not listening
          52 = Duplicate name on network
          53 = Network name not found
          54 = Network busy
          55 = Network device no longer exists
          56 = Net BIOS command limit exceeded
          57 = Network adapter hardware error
          58 = Incorrect response from network
          59 = Unexpected network error
          60 = Incompatible remote adapter
          61 = Print queue full
          62 = Not enough space for print file
          63 = Print file deleted
          64 = Network name deleted
          65 = Access denied
          66 = Network device type incorrect
          67 = Network name not found
          68 = Network name limit exceeded
          69 = Net BIOS session limit exceeded
          70 = Temporarily paused
          71 = Network request not accepted
          72 = Print/disk redirection paused
          80 = File already exists
          82 = Cannot make directory entry
          83 = Interrupt 24H failure
          84 = Too many redirections
          85 = Duplicate redirection
          86 = Invalid password
          87 = Invalid parameter
          88 = Network device fault
 
*    EMS Error Codes:
 
         128 = Internal error in EMM software
         129 = Malfunction in EMM hardware
         131 = Invalid Emshandle%
         132 = Undefined Operation%
         133 = No more handles available
         134 = Error in save/restore of mapping context
         135 = No more pages physically available
         136 = No more pages logically available
         137 = Zero pages requested
         138 = Invalid Emspage% for this Emshandle%
         139 = Invalid Emspage% in range 0-3
         140 = Page-mapping hardware state save area is full
         141 = Save of mapping context failed. Save area contains
               context associated with this handle.
         142 = Restore of mapping context failed. Save area does not
               contain context for this handle.
         143 = Subfunction parameter not defined

     Please Note:  BOBSLED doesn't use any EMS, these are included only 
                   for completeness of this topic.
     

     
*    Error Messages:

     In various places throughout BOBSLED, Error Handling will  display
     messages from time to time.  Although we've had little  success in
     actually producing errors in BOBSLED, these are some  that we have
     been able to document.  As users of  BOBSLED  report  other errors
     we will add them to this text in later version releases.

     Should you encounter an unidentified error, please contact us.  We
     will need to know  the  type  of  system  you are using, where the
     error took place,  "circumstances,"  and  the  error number.  Full
     Motion Net, Thanks You, in  advance  for  your  support  in making
     BOBSLED a better program.

     Known BOBSLED Errors:

     1.   Error # 217 during printing large documents.

          This is determined to be a print buffer  device  error.  Too 
          much  data  is  being sent to the printer, or the printer is 
          telling BOBSLED to "hold up."  
          
          Click the "OK," and printing will  resume.  This  error  has 
          been trapped internally  by  BOBSLED,  and  is  counted.  In 
          others words, you can get  this error up to 5 times during a 
          print run before BOBSLED, will abort the run.

     2.   Error # 262 "Invalid Handle"

          You  tried to Print a Subroutine, however you never selected 
          one, first.

          Click the "OK," select an item, then retry.

     3.   You may encounter instances when the actual ROW number differs
          with the  ROW  number  that  BOBSLED  reports.   Once you have
          paged down through  your  document,  once,  BOBSLED will self-
          adjust  to  the  correct  ROW.   This problem will most likely 
          occur when using documents exceeding 4000 lines.
     
     

                                -END OF HELP.DOC-