Ex -- the External transfer protocol CD-ROM download driver.
  Program and documentation (C) Copyright 1994 Strange Systems.

*******************************************************************************
Ex is released as shareware.  User is granted a 14 day evaluation period.
Usage after 14 days requires registration.  Registration for Ex and all future
updates to Ex is (in US funds) $10 for non-commercial users up to 5 lines, $20
for non-commercial users over 5 lines, and $25 for commercial users, unlimited
lines.  For this document, commercial users are defined as any system
requiring pay-for-access of any kind.

The standard registered version of Ex supports up to 25 Volumes and copies up
to 25 files per run; custom versions are available on request for additional
cost.  Send registrations to:

                 Roger Morris
                 PO Box 52183
                 Shreveport, LA 71135-2183

(We are working towards credit card and online registrations)
*******************************************************************************

Purpose
  Ex was designed to copy files off of CD-ROM drives before downloading them.
  Works with all external transfer protocols that use a redirection file for
  the download list, via the @ character and is host (BBS) software independant.
  Ex needs a config file to determine your system setup; default is Ex.Cfg but
  can be overridden by the -c command line option.

Operation
  Ex tracks and sorts by drive up to 50 files per session, and copies up to 5
  files as needed, loads the transfer driver, and deletes the copied files
  before returning to the host program.  Registered versions copy up to 25
  files per session.  The errorlevel returned from Ex is whatever the transfer
  program exited with.  If the file transfer module didn't load, then 255 is
  returned.  Running Ex with no parameters brings up a blurb screen and exits
  with errorlevel 0.

OS/2 or DOS
  Ex comes in both native OS/2 32-bit and DOS 16-bit versions.  Both versions
  use the same config file and utilize a temporary file named Ex.Tmp that is
  created in the same directory as the redirection file.

Command line
  Ex reads the command line for an alternate config file and the redirection
  file.  Everything after the config file entry is expected to be a transfer
  driver filename and it's associated parameters.  Ex reads and, if needed,
  rewrites the redirection file.  A typical command line is:

  Ex [-cConfig.Fil] FZmodem sz -rr @D:\BBS\Node5.Lst

  This would tell Ex to read configuration file 'Config.Fil' in the current
  directory, then to run FZmodem to transfer files listed in D:\BBS\Node5.Lst.
  
  Example PROTOCOL.CTL entries for Maximus BBS and DSZ:
    Protocol Zmodem
    [...]
    Download   Ex Dsz port %P speed %W estimate 0 %b ha rts -Z sz @dsz%k.ctl
    [...]
    End Protocol
  Or, for multi node systems:
    Protocol Zmodem
    [...]
    Download   Ex -cEx%k.Cfg Dsz port %P speed %W estimate 0 %b ha rts -Z
     sz @dsz%k.ctl
    [...]
    End Protocol

Config file
  The default config file is Ex.Cfg located in the current directory, and
  needs only 2 verbs -- CopyDir and Volume.  Only one CopyDir is permitted but
  up to 5 Volumes (25 in registered version) are supported.  A cut-and-paste
  example config file is:

  ; Sample config file for Ex
  ;  (All verbs must begin in first column!)
  ;
  ; Where to copy files to ...
  CopyDir C:\Temp
  ;
  ; Drives that we want to copy from and not download directly off of
  Volume P:
  Volume Q:
  Volume R:\
  ; Alternate method for CD-ROM servers:
  Volume \\Cd-Server\CD-1
  Volume \\Cd-Server\CD-2
  ;
  ; Maximum limits: 1 CopyDir, 5 Volumes.  (Registered version is 25 Volumes)
  ;
  ; End of Ex.Cfg


Multi-Node
  Ex will run multi-node with either a single config file or a config file for
  each node.  Ex will only delete the files it copied, so all nodes can share
  the same CopyDir directory.  Should the same file be downloaded from
  multiple nodes simultaneously, Ex will only copy the file once for the first
  node that exits to download, the others will still download off of CD-ROM.
  This is a safety feature; if EX can't copy a file it leaves the redirection
  file unchanged and downloads from CD-ROM will be downloaded from CD-ROM.


Warranty
*******************************************************************************
  No warranty, expressed nor implied.  User determines usability of program
  and assumes all responsibilities for the usage of this program.  Feedback is
  welcomed.  Send feedback to the above US Mail address, or electronic mail to
  FidoNet 1:380/25 or 1:380/5, internet remus@f25.n380.z1.fidonet.org  Support
  sites are Strange Systems at 318-869-4006 or MSG Resources at 318-865-4503.
  Latest version of Ex can be found on either of these systems in the STRANGE
  download directory or file requested as 'EX' from either system.
*******************************************************************************

  (Maximus (C)Copyright Scott Dudley, DSZ (C)Copyright Omen Technologies)