File:	KSPBOOT.A, KSPBOOT.EXE

Legal:	Freeware, but copyrighted!  Not to be used in a commercial
	product, or sold for a profit.  Otherwise, no restriction.

What:	A TSR that monitors a com port and reboots the computer if
	four rings go unanswered.

Why:	I didn't like what was already available.  This code is
	different in that it actually detects TRANSITIONS on the
	Ring Indicator status bit of the serial port, rather than
	simply sampling it periodically for a ringing status. This
	code also resets the running ring count after five seconds
	of no rings.  Code accomplishes reboot by asking the keyboard
	controller to activate the cpu reset line rather than jumping
	to FFFF:0000 since the latter doesn't work if a Novell server
	is running! :-)  Thus a 286 or better is required. :-(

How:	First use: "KSPBOOT COMn", where 'n' is a number between 1
	and 4.  This simply installs the TSR, but doesn't activate
	it.  Subsequent use: "KSPBOOT ON" or "KSPBOOT OFF"; enables
	or disables the TSR.

Who:	Dan Lewis			Phone: (415) 364-9847
	Key Software Products		Answered by voice mail
	440 Ninth Avenue		during working hours, BBS
	Menlo Park, CA 95053		at all other times.

Note:	The source code was assembled with the assembler that comes
	with the DeSmet C88 compiler.  To rebuild the code:

	ASM88 KSPBOOT
	BIND -A KSPBOOT

Enjoy!