(C) '94 CARD GUIDE     GLOSSARY OF TERMS/KEY TO ABREVIATIONS

COMMON SERIAL PORT ADDRESSES                      PRINTER PORT ADDRESSES
----------------------------                      ---------------------- 
COM1 - 3F8  NORMALLY IRQ4                         * LPT1: 378  IRQ7
COM2 - 2F8  NORMALLY IRQ3                           LPT2: 278  IRQ5 
COM3 - 3E8  NORMALLY IRQ4 (SHARED WITH COM1)         
COM4 - 2E8  NORMALLY IRQ3 (SHARED WITH COM2)      * ON SOME BRAND NAME PCS
                                                    LPT1 WILL BE AT 3BC


MULTI I/O - SPECIFIES A CARD THAT HAS TWO OR MORE I/O FUNTIONS BUILT 
            ONTO IT.  USUALLY THE FUNCTIONS WILL BE A COMBINATION OF SERIAL, 
            PARALLEL, AND GAME/JOYSTICK PORT.

IDE MULTI I/O - SPECIFIES A CARD THAT INCLUDES EVERYTHING THE ABOVE 
                MULTI I/O HAS PLUS AN IDE HARD DRIVE INTERFACE AND USUALLY 
                A FLOPPY DRIVE INTERFACE AS WELL.

SERIAL I/O - SPECIFIES A CARD THAT HAS ONLY SERIAL PORTS

IDE AND FDC I/O ONLY - SPECIFIES A CARD THAT HAS ONLY HAS IDE HARD DRIVE 
                       AND FLOPPY DRIVE I/O PORTS
 
ENA - SPECIFIES THE SETTING FOR ENABLING THE PORT

DIS - SPECIFIES THE SETTING FOR DISABLING THE PORT

SEL - ABBREVIATION FOR SELECT

JPX - ABBREVIATION FOR JUMPER (X IS NO. THAT IS LABELLED ON CARD)

CN - ABBREVIATION FOR CONNECTOR

PRI - ABBREVIATION FOR PRIMARY (OR MAIN) SETTING OF PORT

SEC - ABBREVIATION FOR SECONDARY SETTING OF PORT

IDE - SPECIFIES THE IDE HARD DRIVE PORT

FDC/FDD - SPECIFIES THE FLOPPY DISK CONTROLLER OR DRIVE PORT

COM1/3 - SPECIFIES THE SERIAL PORT WHICH IS SWITCHABLE BETWEEN COM1 AND 
         COM3

COM2/4 - SPECIFIES THE SERIAL PORT WHICH IS SWITCHABLE BETWEEN COM2 AND 
         COM4

UART - ANOTHER TERM USED TO SPECIFY THE SERIAL PORT USUALLY WHEN IT IS NOT
       CONFINED TO BEING ANY SPECIFIC COM NUMBER.

LPT - SPECIFIES THE PARALLEL PORT

GAME - SPECIFIES THE JOYSTICK PORT

LED - SPECIFIES THE CONNECTOR TO WHICH THE HARD DRIVE LIGHT (LED) IS 
      CONNECTED

IRQ - SPECIFIES AN INTERRUPT REQUEST LINE SETTING

RS232/ASYNC - OTHER TERMS SOMETIMES USED TO DESCRIBE SERIAL CARDS AND 
              PORTS