April 1994



                    FCC Frequency Allocations
                   ---------------------------
    A summary of the FCC Table of Frequency Allocations, based on
    the Oct '91 Code of Federal Regulations  -  47 CFR 2.106



  30 - 50 MHz:  FM @ 20 kHz steps
      30.010 -  30.550  US Government
      30.560 -  31.980  Business / Industry / Forestry
      31.990 -  32.000  Public Safety
      32.010 -  33.000  US Government
      33.000 -  33.100  Public Safety
      33.120 -  33.400  Business / Petroleum
      33.420 -  34.000  Fire
      34.000 -  35.000  US Government
      35.020 -  36.000  Business / Paging
      36.000 -  37.000  US Government
      37.020 -  37.420  Police / Public Service
      37.460 -  37.860  Power, Water, Pipeline
      37.900 -  38.000  Highway Maint / Special Emergency
      38.000 -  39.000  US Government
      39.020 -  40.000  Police / Public Service
      40.000 -  42.000  US Government
      42.020 -  42.940  State Police
      42.960 -  43.680  Business / Paging
      43.700 -  44.600  Transportation - bus, truck
      44.620 -  45.060  State Police / Forestry Conservation
      45.080 -  45.860  Police / Local Govt / Highway Maint
      45.900 -  46.040  Police / Emergency
      46.060 -  46.500  Fire
      46.520 -  46.580  Local Govt
      46.610 -  46.970  Cordless Phones - base        (30 kHz steps)
      47.020 -  47.400  Highway Maint
      47.440 -  47.680  Industry / Emergency
      47.700 -  49.580  Industry
      49.610 -  49.970  Cordless Phones - handset     (30 kHz steps)

  50 - 150 MHz
      50.000 -  54.000  Amateur (6-meters)
      54.000 -  72.000  Broadcast TV   chs 2-4        (6 MHz steps - FMw)
      72.000 -  76.000  (various)
      76.000 -  88.000  Broadcast TV   chs 5-6        (6 MHz steps - FMw)
      88.000 - 108.000  FM Broadcast                  (200 kHz steps - FMw)
     108.000 - 118.000  Aero - navigation
     118.000 - 136.000  Aero - communications         (25 kHz steps - AM)
     136.000 - 138.000  Satellite
     138.000 - 144.000  US Government
     144.000 - 148.000  Amateur (2-meters)
     148.000 - 150.800  US Government

  150 - 162 MHz:  FM @ 15 kHz steps
     150.815 - 150.965  Auto Emergency
     150.995 - 151.595  Highway / Forestry / Industry
     151.625 - 151.955  Business                      (30 kHz steps)
     152.030 - 152.240  Mobile Telephone (Base)       (30 kHz steps)
     152.270 - 152.450  Taxi (Base)
     152.495 - 152.855  Mobile Telephone (Base)       (30 kHz steps)
     152.870 - 153.725  Industry
     153.740 - 154.445  Fire / Govt (mobile)
     154.452 - 154.481  Govt / Industry (telemetry)   (7.5 kHz steps)
     154.490 - 154.625  Industry
     154.650 - 156.240  Police / Govt / Emrgncy / Hwy
     156.025 - 157.425  Maritime (ship)               (25 kHz steps)
     157.470 - 157.515  Auto Emergency
     157.530 - 157.710  Taxi (mobile) / Business
     157.770 - 158.100  Mobile Telephone (mobile)     (30 kHz steps)
     158.130 - 158.460  Industry
     158.490 - 158.670  Mobile Telephone (mobile)     (30 kHz steps)
     158.730 - 158.210  Police / Govt / Highway
     159.225 - 159.465  Forestry Conservation
     159.495 - 160.200  Transportation - bus, truck
     160.215 - 161.610  Railroad
     160.625 - 160.950  Maritime - Coast              (25 kHz steps)
     161.640 - 161.760 {Broadcast Pickups
     161.500 - 162.025 {Maritime - Coast              (25 kHz steps)

  162 - 450 MHz
     162.025 - 174.000  (various, mainly US Government)
     174.000 - 216.000  Broadcast TV  chs 7-13        (6 MHz steps - FMw)
     216.000 - 220.000  Maritime                      (25 kHz steps)
     220.000 - 222.000  (Private land Mobile)
     222.000 - 225.000  Amateur
     225.000 - 400.000  US Government - Aero          (AM)
     400.000 - 406.000  US Govt - Meteorlogical / Space
     406.000 - 420.000  US Government
     420.000 - 450.000  Amateur / military radar

  450 - 460 MHz:  FM @ 25 kHz steps  (450-455 base, 455-460 mobile)
     450.050 - 450.925  Auxiliary Broadcasting
     451.025 - 451.275  Power / Industry
     451.300 - 451.500  Telephone Maint / Industry
     451.525 - 452.025  Industry / Special Industrial
     452.050 - 452.500  Taxi / Industry / Transport
     452.525 - 452.600  Automobile Emergency
     452.625 - 452.950  Transportation - Trucks / Railroad
     452.975 - 453.000  Relay Press
     453.025 - 453.975  Local Govt / Public Safety
     454.025 - 454.650  Mobile Telephone
     454.675 - 454.975  Mobile Telephone Air
     455.050 - 455.925  Auxiliary Broadcasting
     456.025 - 456.275  Power / Industry
     456.300 - 456.500  Telephone Maint / Industry
     456.525 - 457.025  Industry / Special Industrial
     457.050 - 457.500  Taxi / Industry / Transport
     457.525 - 457.600 {Maritime - shipboard repeater
                       {Business - low power
     457.625 - 457.950  Transportation - Trucks / Railroad
     457.975 - 458.000  Relay Press
     458.025 - 458.975  Public Safety / Local Govt
     459.025 - 459.650  Mobile Telephone
     459.675 - 459.975  Mobile Telephone Air

  460 - 470 MHz:  FM @ 25 kHz steps  (460-465 base, 465-470 mobile)
     460.025 - 460.550  Police / Public Safety
     460.575 - 460.625  Fire
     460.650 - 460.875  Business - Airport use
     460.900 - 461.000  Business - Central Alarms
     461.025 - 462.175  Business
     462.200 - 462.525  Manufacturers / Industry
     462.550 - 462.725  GMRS
     462.750 - 462.925  Business (paging)
     462.950 - 463.175  MED (Ambulance/Hospital)
     463.200 - 465.000  Business
     465.025 - 465.550  Police / Public Safety
     465.575 - 465.625  Fire
     465.650 - 465.875  Business - Airport use
     465.900 - 466.000  Business - Central Alarms
     466.025 - 467.175  Business
     467.200 - 467.525  Manufacturers / Industry
     467.550 - 467.725  GMRS
     467.750 - 467.925 {Business (low power)
     467.750 - 467.825 {Maritime - shipboard
     467.950 - 468.175  MED  (Ambulance/Hospital)
     468.200 - 469.975  Business

  470 - 806 MHz:  6 MHz per channel, wide FM audio
     470.000 - 512.000 {Broadcast TV, chs 14-20
                       {Large Metro Public Safety     (25 MHz steps - FM)
     512.000 - 806.000  Broadcast TV, Chs 21-69

  806 - 896 MHz:  FM @ 25 kHz steps  (mobile 806-851, base 851-896)
     806.000 - 809.750  General - conventional
     809.750 - 816.000  General - trunked
     816.000 - 821.000  SMR - trunked
     821.000 - 824.000  Public Safety - trunked       (12.5 kHz steps)
     824.040 - 834.360  Cellular Telephone            (30 kHz steps)
     834.390 - 835.620  Cellular Telephone (data)     (30 kHz steps)
     835.650 - 848.970  Cellular Telephone            (30 kHz steps)
     849.000 - 851.000  Aircraft Telephone            (5 kHz steps - AM)
     851.000 - 854.750  General - conventional
     854.750 - 861.000  General - trunked
     861.000 - 866.000  SMR - trunked
     866.000 - 869.000  Public Safety - trunked       (12.5 kHz steps)
     869.040 - 879.360  Cellular Telephone            (30 kHz steps)
     879.390 - 880.620  Cellular Telephone (data)     (30 kHz steps)
     880.650 - 893.970  Cellular Telephone            (30 kHz steps)
     894.000 - 896.000  Aircraft Telephone            (5 kHz steps - AM)

  896 - 941 MHz
     896.000 - 901.000  Business / Industry / SMR     (12.5 kHz steps)
     901.000 - 902.000  General Purpose Mobile Radio
     902.000 - 935.000  ()
     935.000 - 940.000  Business / Industry / SMR     (12.5 kHz steps)
     940.000 - 941.000  General Purpose Mobile Radio