MHSPING: send pings to specified hosts and waits for an echo
                  ver 0.30 - (c) Grouper Technologies 1994

***FREEWARE*** you may copy and share this program as long as no money is
               involved (except for media and shipping expenses)

 Object:

     - PING is an MHS gateway that sends dummy messages (pings) to
       a list of target hosts and waits for an echo.

     - PING holds statistical data for each target host: average
       delay between sending the ping and receiving the echo, and number
       of hops between the pinging host and the target host.

     - PING warns the MHS administrator if no echo is received from a
       target host after four times the average echo delay for this host.

       PING was developped to enhance MHS host communication reliability
       by detecting when a distant host is down.


 Syntax:

       Install the PING gateway with the PGINST batch file, and run the
       MHSPING program manually to display statistical information.

       To the PING gateway, invoke the PGINST batch with the name(s) of
       the MHS host(s) you want to test automatically. For example
       "PGINST FARHOST" will install the PING gateway and test host
       FARHOST.

       Alternatively, PING can accept the name of a file containing a
       list of hosts as a parameter. In this case the file should be
       located in the gateway's PUBLIC directory, and its name should
       be preceeded by a '@' sign in the "Gateway commands" field
       (extension should be supplied if necessary).

       For example, if you create a host-file "HOSTS.TXT" in the
       MHS\MAIL\GATES\PING\PUBLIC directory, invoke the command
       "PGINST @HOSTS.TXT" to re-install the PING gateway with the correct
       parameter. Hosts names and host-file name(s) can be mixed in the
       gateway parameters. The host-file format is pure ASCII, one host
       name per line.

       To add or delete hosts to be tested by PING after installation,
       run the MHS directory manager and add or delete host names in the
       "Gateway commands" field for the PING gateway. If you use an
       alternate host-file, add or delete host names in this file.

       Here is an example of a statistical output displayed when manually
       invoking the MHSPING program (after the gateway has been installed
       and run at least once):

                Host name        : FARHOST
                Last ping sent   : Wed Jan 19 16:38:53 1994
                Average delay    : 36 minutes
                Hops (one way)   : 2
                Warning threshold: 3 hours


       The PING gateway can be used in conjunction with the MHS Scheduler
       from Infinite Technologies or other equivalent utilities, to be
       invoked for example once a day.


 Files:
       MHSPING.EXE copied in MHS/MAIL/GATES/PING/PUBLIC as INPOST.EXE
       MHSPING.EXE copied in MHS/EXE
       PING.DAT created in MHS/MAIL/PUBLIC by the gateway


 Internals:

       A dummy user routing is created to route echoes to the gateway.
       PING has only been tested with MHS 1.5 hosts.
       Host CSERVE does not echo any ping (stealth hub?)...


 Changes:
       Version 0.30: added support for host files
                     changed executable name to MHSPING.EXE
       Version 0.20: added support for FS/VOL in MV variable
       Version 0.10: initial release

 Author:
       Francois Bergeon
       Grouper Technologies
       MHS: FBERGEON @ GROUPMNT
       Internet: fbergeon@groupmnt.mhs.compuserve.com
       CIS: 73377,3170


 Thanks to:
       Brett Warthen (Infinite Technologies) for the idea...