============================================================================
                CalcuFret v1.0          c1994 Trevor Boicey
============================================================================

ONE LINE DESCRIPTION:

  CALCUFRT.ZIP : Computes fret scales for musical instruments.

REQUIREMENTS:

  An MSDOS compatible machine or emulator. Very little memory is
  needed, I can't imagine any machine that WON'T run this program.

  A printer is also handy for making hard copies of data to
  keep beside you in the workshop. Lots easier than doing
  precision woodworking on your computer table.

WHAT THIS PROGRAM DOES:

  This program is for building and working with guitars, basses,
  and other musical instruments.

  You provide the program with data about the instrument you
  are working with, and the program will provide the precise
  locations of all the frets for that particular instrument.

  CALCUFRT can be used to find the fret slots to build a
  guitar from scratch, or to install a new fretboard, or
  for fret crowning, or any time you need to mathematically 
  locate the frets of an instrument accurately.

  This program is also useful for first time fretless or
  orchestral musicians. With the help of this program, you
  can "find" the notes on your instrument, where you can
  then place stickers or nail polish to learn where the
  notes are.

  Although most luthiers will only use 12 frets per octave for
  "western" music, the program can produce charts for any number
  of frets per octave, which may be useful to luthiers producing
  experimental or traditional instruments.

USING THE PROGRAM:

  To run the program, type "CALCUFRT" at the DOS prompt.

  The program will bring up a screen with two requesters,
  labelled "SCALE LENGTH" and "FRETS PER OCTAVE". This is
  all the information that CalcuFret will need to perform
  the calculations.

  When the program is first run, the FRETS PER OCTAVE will
  show 12, and the requester will be open in the SCALE LENGTH
  entry. Use the up and down cursor keys to select the
  scale length of the instrument you are working with. Common
  values for six string guitars are 24-26 inches, for electric
  basses, 30-36 inches, etc.

  The "SCALE LENGTH" is officially the distance between the
  nut and the bridge, before intonation is considered. In the
  real world of course, the intonation will necessitate this
  distance be a bit longer. But the scale length is this
  nut-bridge distance, or equivalently, twice the distance
  between the nut and the octave fret. (usually 12th)
  
  For example, to fret an electric bass, you might 
  desire a 34 inch scale. You would then use the up and down
  arrow keys until the highlighted line in the requester was
  over 34.

  To change the number of FRETS PER OCTAVE, simply press the
  right arrow key. The scale requester will close, and show
  the scale selected. The FRETS PER OCTAVE requester will
  then open, and the desired value can be selected like with
  the scale length. You can also use the left/right arrow
  keys to toggle between the two requestors until you are
  satisifed with both settings.

  ( Do not confuse frets per octave with total frets. Calcufret
    will show the first 48 frets regardless of this setting, which
    is more than enough for any instrument I've ever seen. You
    need only use the number of frets you wish to install on
    your instrument. Therefore for a 22 fret guitar, FRETS PER
    OCTAVE must still be at 12, and you would only use the
    info provided for the first 22 frets. )

  When you are satisfied that both requestors contain the right
  information for your instrument, pressing RETURN accepts the
  data and will cause CalcuFret to make the calculations on
  those values.

OUTPUT SCREEN:

  The output screen basically shows the results of all the 
  calculations. It contains all the data you should need
  to fret an instrument.

  To make a hard copy of this screen, have your printer
  attached and configured normally, and press SHIFT-PrtSc
  to print the screen in the usual DOS way.

  To Re-Run the program, perhaps to fine-tune the input,
  or experiment with new values, press SPACE.

  To exit the program, hit ESC.

INTERPRETING THE RESULTS:

  The output screen shows three colums of data, each column has
  16 frets, for a total of 48 frets. Again, unless you are using
  24 frets per octave or more, this is probably way more than
  you will need.

  Each fret number has two measurements beside it. One is the
  width of that fret from the previous one, the other is
  the cumulative distance of that fret from the nut.

  Example:

    Select a scale length of 34 inches, twelve frets per octave.

    The output will be similar to:

    Fret   Width   Cumul.
      1    1.908   1.908
      2    1.801   3.709
      3    ....etc

    Therefore, you would measure 1.908 inches from the nut,
    and scribe a line. This will be the first fret.

    Next, measure 1.801 inches from the scribed line
    where the first fret will be. Scribe a line, this
    is fret two. Now measure from the second fret to
    the nut, and check that the distance is 3.709 inches.
    
    If so, the fret is correct, you can now move on until all 
    frets are marked.

LEGAL INFO:

  - This program can be used free of charge, and distributed
    by most any method, as long as no fee is charged. Feel
    free to send this program to FTP sites, BBSs, etc.

    All I ask is that the archive is kept together, so that the
    program and this doc file are always present.

  - This program, as far as I know, works great. The results
    it produces collaborate with tables from books on
    guitar making that I own. 
    
    *BUT* 
    
    I am in no way responsible for the accuracy of this information. 
    
    Use at your own risk.

OTHER INFO:

  - The "SCALE LENGTH" need not be in inches, if you prefer
    to work in something else, like centimeters. The results
    are in the same units that the input is given in.

    If you wanted an instrument with a scale of 90cm, just
    enter 90 as scale length, and read the results in
    centimeters as well.

  - I can be reached via email at "ae718@freenet.carleton.ca"
    for at least a while. It's mid 1994 right now, if you get
    this much later than that, I don't know where I'll be.

    Feel free to email me about this program. If you can't get
    it to work, tell me a bit about your machine, I'll see what
    I can do.

    If you have anything in mind that should be added to this
    program, by all means get in touch. I'd like to expand it
    to use non-tempered fret scales or other uncommon scales
    as well, but frankly I don't have the mathematical info
    myself. If you do, email me, and I'll make CalcuFret be
    able to work with these as well.

  - Enjoy!

============================================================================