===========================================================
                DDDDD           DDDDD               SSSS
                 D   Dunfield    D   D             S
                 D   D           D   Development    SSSS 
                 D   D           D   D                  Systems
                DDDDD           DDDDD               SSSS
          ===========================================================
          MM   MM  IIIIIII    CCCC   RRRRRR     OOO             CCCC
          M M M M     I      C    C  R     R   O   O           C    C
          M  M  M     I     C        R     R  O     O         C
          M     M     I     C        RRRRRR   O     O  -----  C
          M     M     I     C        R   R    O     O         C
          M     M     I      C    C  R    R    O   O           C    C
          M     M  IIIIIII    CCCC   R     R    OOO             CCCC
          ===========================================================
    
    
    
    
    
                             A compact 'C' compiler
                                      for
                                 Small Systems.
    
    
                               Library Reference
    
    
    
    
    
                                  Release 3.1
    
                               Revised 14-Apr-94
    
    
    
    
    
    
    
    
    
    
    
    
                       Copyright 1988-1994 Dave Dunfield
                              All rights reserved

    MICRO-C Library                                                  Page: 1


    1. THE MICRO-C LIBRARIES
    
          The MICRO-C distribution disk includes the 'C'  and  'ASM'  source
       code for a very complete function library which is configured for use
       on an IBM/PC under the MS-DOS operating system. These routines may be
       also be used as "example" programs, providing  insight  into  MICRO-C
       programming techniques.
    
          All functions except for the lowest level I/O routines  are  coded
       in 'C', and should compile on any MICRO-C system. Note that some  low
       level functions in the library are written in 'C' using  still  lower
       level routines. Although this makes the library highly  portable  and
       reduces the number of routines you have to re-write  for  a  specific
       system, the resultant function will be less efficent than  one  which
       directly uses the operating system services.
    
          If you are implementing MICRO-C an a small system  and  intend  to
       use it for serious programming, I strongly recommend that you re-code
       all of the low level library functions in assembly language.
    
          Note that since library routines are often  used  in  applications
       where code size and execution speed are of primary importance, it may
       be desirable to recode some or all of the other library  routines  in
       assembly language as well.
    
          For those who intend to make only casual use of  MICRO-C,  or  who
       wish to experiment with it simply for the  learning  experience,  the
       'C' versions of the low level library functions should be  more  than
       sufficient.
    
          NOTE: If you purchased MICRO-C as  part  of  a  "developers  kit",
       refer to the documentation included with the CPU  support  files  for
       details on the pre-configured library for that CPU, and the functions
       available therein.

    MICRO-C Library                                                  Page: 2


    
                         +----------------------------+
                         |                            |
                         |  ************************  |
                         |  * The STANDARD library *  |
                         |  ************************  |
                         |                            |
                         +----------------------------+
    
    
    
    
    
    
    
    
    
    
       1.1 STANDARD Library
    
             The library functions described  on  the  following  pages  are
          currently available in the IBM/PC MICRO-C  library  as  "standard"
          functions which are of a general nature, and should be portable to
          most implementations of MICRO-C.
    
             The exact syntax and capabilities of the  system  or  processor
          dependant functions may vary  in  different  implementations,  see
          your  implementation  notes  (READ.ME)  for   details.   Different
          possible forms of such functions are shown using (1), (2), ...  In
          these cases, the form (1) of the function is the one used  in  the
          MS-DOS library.

    ABORT                                                             ABORT
    
    
    
    PROTOTYPE:
    
        abort(char *message)
    
    
    ARGUMENTS:
    
        message - Pointer to message to display
    
    
    RETURN VALUE:
    
        N/A - Function never returns
    
    
    DESCRIPTION:
    
          This function writes the string passed as an argument to  standard
       error, and then terminates the program with a  return  code  of  '-1'
       (Indicating general  failure).  This  provides  a  simple  method  of
       terminating a program on an error condition with a message explaining
       why.
    
    
    EXAMPLES:
    
        abort("Invalid operand\n");

    ABS                                                                 ABS
    
    
    
    PROTOTYPE:
    
        int abs(int number)
    
    
    ARGUMENTS:
    
        number  - Any integer value
    
    
    RETURN VALUE:
    
        The absolute value of "number"
    
    
    DESCRIPTION:
    
          The "abs" function returns the absolute value of the argument.  If
       "number" is a positive value, it is returned unchanged. If  negative,
       the negate of that value is returned (giving a positive result).
    
    
    EXAMPLES:
    
        difference = abs(value1 - value2);

    ATOI                                                               ATOI
    
    
    
    PROTOTYPE:
    
        int atoi(char *string)
    
    
    ARGUMENTS:
    
        string  - Pointer to a string containing a decimal number
    
    
    RETURN VALUE:
    
        16 bit integer value
    
    
    DESCRIPTION:
    
          The "atoi" function converts an ASCII string containing  a  signed
       decimal number (-32768 to 32767) to a 16 bit value which is returned.
       An unsigned number of the range (0 to 65535) may also  be  used,  and
       the result if assigned to an "unsigned" variable will be correct.
    
    
    EXAMPLES:
    
        value = atoi("1234");
        value = atoi("-1");

    BSEARCH                                                         BSEARCH
    
    
    
    PROTOTYPE:
    
        char *bsearch(char *k, char *t, unsigned e, unsigned s, int (*f)())
    
    
    ARGUMENTS:
    
        k   - Key to search for
        t   - Table to search
        e   - Number on entries in the table
        s   - Size of each entry
        f   - Pointer to function performing compare
    
    
    RETURN VALUE:
    
        Address of found record, or zero (0) if no match
    
    
    DESCRIPTION:
    
          Performs a binary search of the specified table, looking  for  the
       given key.  Since  this  is  a  binary  search,  the  table  must  be
       maintained in sequential order with lower entries appearing first.
    
          Any fixed format table can be used. The key and a pointer to  each
       entry to test are passed to the user supplied compare function, which
       must return 0 if equal, <0 if the key (first arg) is  less  than  the
       table entry, or >0 if the key is larger than the table entry.
    
    
    EXAMPLES:
    
        #include <stdio.h>
        int table[] = { 123, 187, 236, 392, 481, 599, 600, 737 };
        int test(int *a, int *b) { return *a - *b; }
        main(argc, char *argv[])
        {
            int key;
            key = atoi(argv[1]);
            printf("%04x", bsearch(&key, table, 8, sizeof(int), &test));
        }

    CALLOC                                                           CALLOC
    
    
    
    PROTOTYPE:
    
        char *calloc(int size)
    
    
    ARGUMENTS:
    
        size    - Size of memory block to allocate (in bytes).
    
    
    RETURN VALUE:
    
        0       - Memory allocation failed
        !0      - Pointer to allocated memory block
    
    
    DESCRIPTION:
    
          The "calloc" function allocates a block of memory of the specified
       size from the heap, and returns a pointer to it. The allocated memory
       is automatically cleared to zeros. This memory will remain  allocated
       until it is explicitly released with the "free" function.
    
    
    EXAMPLES:
    
        if(!(ptr = calloc(BUFSIZ)))     /* Allocate a temporary buffer */
            abort("Not enough memory");
        do {                            /* Copy the file over */
            size = fread(ptr, BUFSIZ, in_fp);
            fwrite(ptr, size, out_fp); }
        while(size == BUFSIZ);
        free(ptr);                      /* Release temporary buffer */

    CD                                                                   CD
    
    
    
    PROTOTYPE:
    
        int cd(char *pathname)
    
    
    ARGUMENTS:
    
        pathname- Name of directory to make current
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          This function sets the "current" directory, causing all subsequent
       file references which do not explicitly indicate a directory path  to
       access the path specified by "pathname".
    
    
    EXAMPLES:
    
        cd("/mc/c_source");     /* UNIX */
        cd("\\mc\\l_source");   /* MS-DOS */

    CLOSE                                                             CLOSE
    
    
    
    PROTOTYPE:
    
        close(HANDLE fh);
    
    
    ARGUMENTS:
    
        fh      - File handle of an open file
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function closes a file  which  was  previously  opened  using
       "open".
    
    
    EXAMPLES:
    
        close(fh);

    CONCAT                                                           CONCAT
    
    
    
    PROTOTYPE:
    
        register concat(char *dest, char *source, ...)
    
    
    ARGUMENTS:
    
        dest    - Pointer to destination string
        source  - Pointer to source string
        ...     - Additional sources may be given
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "concat" function concatinates the given source  strings  into
       one destination string. The destination string must be  large  enough
       to hold all of the source strings plus the string  terminator  (zero)
       byte. No value is returned.
    
          NOTE: This function uses a variable number of arguments, and  must
       be declared as "register" (See "stdio.h").
    
    
    EXAMPLES:
    
        concat(filename,"/tmp/", input_name);

    CORELEFT                                                       CORELEFT
    
    
    
    PROTOTYPE:
    
        unsigned coreleft()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        Amount of memory remaining on the heap
    
    
    DESCRIPTION:
    
          Computes the amount of memory  available  for  allocation  on  the
       heap.
    
          The highest memory address allocated on  the  heap  is  subtracted
       from  the  stack  pointer,  along  with  a  protective  "margin"  for
       potential stack growth.
    
          The value returned is approximate, and will continue to  vary  due
       to stack use.
    
          Every call to "calloc/malloc" will reduce  the  amount  of  memory
       left in the heap by 3 plus the size of the memory allocated bytes.
    
    
    EXAMPLES:
    
        printf("There is enough memory to allocate %u records\n",
            coreleft() / (sizeof(record)+3));

    CREATE                                                           CREATE
    
    
    
    PROTOTYPE:
    
        int create(char *pathname, int attrs)
    
    
    
    ARGUMENTS:
    
        pathname- Name of file to create
        attrs   - Attributes for new file
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          The "create" function creates a new file with the specified system
       attributes.
    
          The meaning of the individual bits in the "attrs" value is  system
       dependant, and is defined in the "file.h" header file.
    
    
    EXAMPLES:
    
        create("temp", HIDDEN);

    DELETE                                                           DELETE
    
    
    
    PROTOTYPE:
    
        int delete(char *pathname)
    
    
    
    ARGUMENTS:
    
        pathname- Name of file to delete
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          The "delete" function removes an existing file from the disk.  Any
       disk space occupied by the file is released.
    
    
    EXAMPLES:
    
        delete("temp");

    EXIT                                                               EXIT
    
    
    
    PROTOTYPE:
    
        exit(int rc)
    
    
    ARGUMENTS:
    
        rc      - Termination return code
    
    
    RETURN VALUE:
    
        N/A - Function never returns
    
    
    DESCRIPTION:
    
          This function terminates the execution of the program and passes a
       specific return code back to the  operating  system.  A  return  code
       value of zero is used  to  indicate  successful  program  completion.
       Non-zero return code values may be used to indicate a particular type
       of failure. A value of '-1' is often used to indicate a  non-specific
       failure. Note that  the  "rc"  value  is  very  system  specific,  in
       particular, some systems support only 8 bit return codes,  so  values
       which are greater than 255 should be avoided.
    
    
    EXAMPLES:
    
        exit(0);        /* success */
        exit(-1);       /* failure */

    FCLOSE                                                           FCLOSE
    
    
    
    PROTOTYPE:
    
        fclose(FILE *fp);
    
    
    ARGUMENTS:
    
        fp      - File pointer to an open file
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function closes a file  which  was  previously  opened  using
       "fopen". The I/O buffer space used by the file is  released.  In  the
       case of a file open for write ('w'), the last disk buffer is  flushed
       and written to disk.
    
    
    EXAMPLES:
    
        fclose(fp);

    FFLUSH                                                           FFLUSH
    
    
    
    PROTOTYPE:
    
        fflush(FILE *fp)
    
    
    ARGUMENTS:
    
        fp       File pointer to an open file
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          The "fflush" function flushes the I/O buffers for the  given  open
       file. If the file is opened for WRITE, this causes any data remaining
       in a partially filled output buffer to be written.  If  the  file  is
       opened for READ, this has the effect of throwing away any data  which
       is pending in the input buffer.
    
    
    EXAMPLES:
    
        fputs("Enter you name?", stdout);
        fflush(stdout);         /* Make sure prompt is output */
        fgets(name, 80, stdin);

    FGETC                                                             FGETC
    
    
    
    PROTOTYPE:
    
        int fgetc(FILE *fp)
    
    
    ARGUMENTS:
    
        fp      - File pointer to an input file
    
    
    RETURN VALUE:
    
        Value of a character read from the file (0-255)
        EOF (-1) if end of file or an error condition occurs
    
    
    DESCRIPTION:
    
          This function reads a single character from  an  input  file,  and
       returns it as a positive value in the range of 0 to 255.  A  full  16
       bit value is returned, allowing the  end  of  file  condition  to  be
       distinct from the character value 255.
    
    
    EXAMPLES:
    
        if((c = fgetc(input_file)) == EOF)
            abort("End of file encountered\n");

    FGETS                                                             FGETS
    
    
    
    PROTOTYPE:
    
        char *fgets(char *buffer, int size, FILE *fp)
    
    
    ARGUMENTS:
    
        buffer  - Pointer to string to receive line
        size    - Maximum size of line to read
        fp      - File pointer to an input file
    
    
    RETURN VALUE:
    
        Pointer to "buffer", or 0 if end of file
    
    
    DESCRIPTION:
    
          The "fgets" function reads characters  from  the  specified  input
       file, and places them in the character  buffer  until  one  of  three
       things happens:
    
          1) A NEWLINE character is encountered.
    
          2) The END of the file is encountered.
    
          3) The limit of "size" character is read.
    
          The string is terminated with the standard  NULL  (00)  character.
       The trailing NEWLINE '\n' character is NOT  included  in  the  output
       buffer.
    
    
    EXAMPLES:
    
        fgets(input_line, 80, input_file);

    FIND_FIRST                                                   FIND_FIRST
    
    
    
    PROTOTYPE:
    
        int find_first(char *pattern, int mattrs, char name[], int &sizeh,
                       int &sizel, int &attrs, int &time, int &date)
    
    
    ARGUMENTS:
    
        pattern - File name pattern to match
        mattrs  - File attributes to match
        name    - Address of string to receive file name
        &sizeh  - Address of int to receive high word of size
        &sizel  - Address of int to receive low word of size
        &attrs  - Address of int to receive attributes
        &time   - Address of int to receive time stamp
        &date   - Address of int to receive date stamp
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          This function locates the first file on the disk which matches the
       given pattern. The "mattrs" field specifies  any  special  attributes
       the files must have  in  order  to  be  matched,  use  0  for  normal
       directory searches.
    
          Subsequent files may be located using the "find_next" function.
    
          The above function prototype describes the  MS-DOS  implementation
       of the function. With other operating systems, the function may  have
       slightly  different  parameters,   due   to   differing   information
       available. See your implementation notes.
    
    
    EXAMPLES:
    
        if(find_first(pattern, 0, name, &sh, &sl, &a, &t, &d))
            abort("No matching files found\n");

    FIND_NEXT                                                     FIND_NEXT
    
    
    
    PROTOTYPE:
    
        int find_next(char name[], int &sizeh, int &sizel, int &attrs,
                      int &time, int &date)
    
    
    ARGUMENTS:
    
        name    - Address of string to receive file name
        &sizeh  - Address of int to receive high word of size
        &sizel  - Address of int to receive low word of size
        &attrs  - Address of int to receive attributes
        &time   - Address of int to receive time stamp
        &date   - Address of int to receive date stamp
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          The function must be preceeded by a call to "find_first", and will
       locate the next file on  the  disk  which  matches  the  pattern  and
       attributes given to that function call.
    
          The above function prototype describes the  MS-DOS  implementation
       of the function. With other operating systems, the function may  have
       slightly  different  parameters,   due   to   differing   information
       available. See your implementation notes.
    
    
    EXAMPLES:
    
        do
            printf("%s\n", name);
        while(!find_next(name, &sh, &sl, &a, &t, &d));

    FOPEN                                                             FOPEN
    
    
    
    PROTOTYPE:
    
        FILE *fopen(char *filename, char *options)
    
    
    ARGUMENTS:
    
        filename- Name of the file to open
        options - String containing open options:
                    'a' - Append to file (must use with 'w')
                    'b' - Binary mode (default is text)
                    'q' - Quit { exit(-1) } on failure
                    'r' - Open file for read
                    'v' - Issue error message on failure
                    'w' - Open file for write
    
    
    RETURN VALUE:
    
        File pointer to the file buffer for the open file
        Zero (0) if file could not be opened
    
    
    DESCRIPTION:
    
          This function opens a file for  buffered  input  ('r')  or  output
       ('w'), allowing subsequent I/O operations to read or write the  file.
       If the 'b' option is NOT included, the file is assumed to be  a  TEXT
       file, and appropriate translations  are  made  for  NEWLINE  and  EOF
       interpretation.
    
          The size of the I/O buffer used is established by "fopen" from the
       external variable 'IOB_size',  which  has  a  default  value  of  256
       (bytes). This variable is defined in the 'file.h'  header  file,  and
       may be modified prior to calling this function if you wish to  use  a
       different buffer size.
    
          One I/O buffer is allocated from the heap for each open file. When
       using a large IOB_size value, you must be careful not to consume more
       memory than is available.
    
    
    EXAMPLES:
    
        fp = fopen("input_file", "r");
        fp = fopen("input_file", "rvq");
        IOB_size = 1024*10;         /* Set up a 10K buffer */
        fp = fopen("output_file", "wb");

    FPRINTF                                                         FPRINTF
    
    
    
    PROTOTYPE:
    
        register fprintf(FILE *fp, char *format, arg, ...)
    
    
    ARGUMENTS:
    
        fp      - File pointer to an output file
        format  - Pointer to format string
        arg     - Argument as determined by format string
        ...     - Additional arguments may be required
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This routine performs a formatted print to  a  file  specified  by
       'fp'. The 'format' string is written to the file with  the  arguments
       substituted for special "conversion  characters".  These  "conversion
       characters" are identified by a preceeding '%', and may be one of the
       following:
    
                    b       - Binary number
                    c       - Character
                    d       - Decimal (signed) number
                    o       - Octal number
                    s       - String
                    u       - Unsigned decimal number
                    x       - Hexidecimal number
                    %       - A single percent sign (No argument used)
    
          A numeric "field width" specifier may be placed in between the '%'
       and the conversion character, in which case the value will be  output
       in a field of that width. If the "field width" is a negative  number,
       the output will be left justified in the field, otherwise it is right
       justified. If the field width contains a leading '0', then the output
       field will be padded with zero's, otherwise spaces are used.
    
          If no "field width" is given, the output  is  free  format,  using
       only as much space as required.
    
          NOTE: This function uses a variable number of arguments, and  must
       be declared as "register" (See "stdio.h").
    
    
    EXAMPLES:
    
        fprintf(stderr,"Filename='%s'\n", filename);
        fprintf(stdout,"Address=%04x\n", address);
        fprintf(outfile,"Amount: $%3u.%02u\n", amount / 100, amount % 100);

    FPUTC                                                             FPUTC
    
    
    
    PROTOTYPE:
    
        fputc(char c, FILE *fp)
    
    
    ARGUMENTS:
    
        c       - Any character value
        fp      - File pointer to an output file
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DECRIPTION:
    
          This function writes the character 'c' to the  file  indicated  by
       the file pointer 'fp'.
    
    
    EXAMPLES:
    
        fputc('*', fp);
        fputc('\n', stderr);

    FPUTS                                                             FPUTS
    
    
    
    PROTOTYPE:
    
        fputs(char *string, FILE *fp)
    
    
    ARGUMENTS:
    
        string  - Pointer to a character string
        fp      - FIle pointer to output file
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          The "fputs" function writes the specified string to the  indicated
       output file. The zero terminating the string is NOT written.
    
    
    EXAMPLES:
    
        fputs("Text message", output_file);

    FREAD                                                             FREAD
    
    
    
    PROTOTYPE:
    
        int fread(char *buffer, int size, FILE *fp)
    
    
    ARGUMENTS:
    
        buffer  - Pointer to buffer to receive data
        size    - Number of bytes to read
        fp      - File pointer to an input file
    
    
    RETURN VALUE:
    
        Number of bytes read from file
    
    
    DESCRIPTION:
    
          This function reads a block of data from a file and places  it  in
       memory at the address of "buffer". Data will be read in  either  TEXT
       or BINARY form, depending on how the file was opened. If  the  number
       of bytes returned is less than the number of bytes requested,  either
       the end of the file was encountered or an error condition occured (in
       which case the value will be zero).
    
    
    EXAMPLES:
    
        fread(block, 512, input_fp);

    FREE                                                               FREE
    
    
    
    PROTOTYPE:
    
        free(char *ptr)
    
    
    ARGUMENTS:
    
        ptr     - Pointer to a previously allocated memory block
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "free" function releases (de-allocates) a block of memory that
       was obtained via a call to "calloc/nalloc", and  returns  it  to  the
       heap. This makes it available for use by other memory allocations.
    
    
    EXAMPLES:
    
        if(!(ptr = malloc(BUFSIZ)))     /* Allocate a temporary buffer */
            abort("Not enough memory");
        do {                            /* Copy the file over */
            size = fread(ptr, BUFSIZ, in_fp);
            fwrite(ptr, size, out_fp); }
        while(size == BUFSIZ);
        free(ptr);                      /* Release temporary buffer */

    FSCANF                                                           FSCANF
    
    
    
    PROTOTYPE:
    
        register int fscanf(FILE *fp, char *format, &arg, ...)
    
    
    ARGUMENTS:
    
        fp      - File pointer to an input file
        format  - Pointer to format string
        arg     - Argument as determined by format string
        ...     - Additional arguments may be required
    
    
    RETURN VALUE:
    
        The number of successful matches
        EOF (-1) if end of file or an error condition occurs
    
    
    DESCRIPTION:
    
          This routine reads a line from the specified file and scans it for
       specific values which  are  then  assigned  to  the  passed  argument
       addresses. The types of values  scanned  are  determined  by  special
       "conversion characters" within the "format" string. These "conversion
       characters" are identified by a preceeding '%', and may be one of the
       following:
    
                    b       - Binary number
                    c       - Character
                    d       - Decimal (signed) number
                    o       - Octal number
                    s       - String
                    u       - Unsigned decimal number
                    x       - Hexidecimal number
                    %       - A single percent sign (No argument used)
    
          Before scanning for any value other than '%c', any leading "space"
       or "tab" characters in the input line are automatically flushed.
    
          Scanning of a particular value type will terminate when either the
       end of  the  line  or  a  non-applicible  character  is  encountered.
       Scanning of strings (%s) stops with a "space" or "tab" character, and
       the stored string will be zero terminated.
    
          A numeric "field width" specifier may be placed in between the '%'
       and the conversion character, in which case  scanning  of  the  value
       will  also  terminate  if  that  many  input  characters  have   been
       processed.
    
          Scanning  for  characters  (%c)  assumes  a  "field  width"  of  1
       character unless otherwise specified. If a field width is  specified,
       the output is assumed to be  a  string,  and  a  zero  terminator  is
       appended.

    
    
    
    
    
    
    
    
    
    
          Any other (non-conversion) characters in the  format  string  will
       cause the next character in the input string which is not  a  "space"
       or "tab" to be skipped if it matches that character.
    
          Any variable values from the input line  which  are  not  required
       must be cleared by scanning them into a "dummy" variable.
    
          The most common mistake when using "fscanf" is forgetting  to  use
       the '&'  operator  with  a  simple  variable  argument.  This  causes
       "fscanf" to store the value INDIRECTLY at the  address  contained  in
       that variable (Similar to  using  '*'  with  a  pointer)  instead  of
       storing the value into the actual variable  itself.  Arguments  which
       are array names do not require the '&' operator, since the address of
       the array is already generated by reference to its name.
    
          Unlike "fscanf" in most  other  compiler  libraries,  the  MICRO-C
       function always reads and scans a single line from the input file.
    
          NOTE: This function uses a variable number of arguments, and  must
       be declared as "register".
    
    
    EXAMPLES:
    
        if(fscanf(infile,"%s %s %u", first_name, last_name, &age) != 3)
            abort("Error in user record\n");

    FSEEK                                                             FSEEK
    
    
    
    PROTOTYPE:
    
        (1) int fseek(FILE *fp, int h_offset, unsigned l_offset, int mode)
        (2) int fseek(FILE *fp, int offset, mode)
    
    
    ARGUMENTS:
    
        fp      - File pointer to an open file
        h_offset- Highest 16 bits of offset value
        l_offset- Lowest 16 bits of offset value
        offset  - 16 bit offset value
        mode    - Type of seek
                    0 = Absolute from start of file
                    1 = Signed offset from current position
                    2 = Signed offset from end of file
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          This function positions the operating system internal pointer into
       a file so that any read or write will take  place  at  the  specified
       position in the file.
    
          Most operating systems which support files of > 64K bytes in  size
       will support form (1) of the function, using both high and low offset
       values.
    
          Smaller operating  systems  may  only  support  form  (2)  of  the
       function, allowing seeking of only +/- 32K bytes.
    
          Also, some implementations may not support  all  "modes",  or  may
       only allow unsigned (positive) offsets.
    
    
    EXAMPLES:
    
        fseek(in_file, 0, 2);   /* Advance to end of file */

    FTELL                                                             FTELL
    
    
    
    PROTOTYPE:
    
        (1) int ftell(FILE *fp, int &h_offset, unsigned &l_offset)
        (2) int ftell(FILE *fp, int &offset)
    
    
    ARGUMENTS:
    
        fp      - File pointer to an open file
        h_offset- Address of int to receive high word of offset
        l_offset- Address of int to receive low word of offset
        offset  - Address of int to receive offset
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          This function gets the current read/write position within a  file.
       The position returned indicates the absolute character (byte)  offset
       from the start of the file where the next read  or  write  will  take
       place.
    
          Most operating systems which support files of > 64K bytes in  size
       will support form (1) of the function, returning both  high  and  low
       offset values.
    
          Smaller operating  systems  may  only  support  form  (2)  of  the
       function,  allowing  access  to  only  the  first   65535   character
       positions.
    
    
    EXAMPLES:
    
        ftell(fp, &oldh, &oldl);    /* Save file position */
            . . .                   /* Perform some operations on the file */
        fseek(fp, oldh, oldl, 0);   /* Return to previous position */

    FWRITE                                                           FWRITE
    
    
    
    PROTOTYPE:
    
        int fwrite(char *block, int size, FILE *fp)
    
    
    ARGUMENTS:
    
        block   - Pointer to a block of data to write
        size    - Number of bytes to write
        fp      - File pointer to an output file
    
    
    RETURN VALUE:
    
        The number of bytes written to the file
    
    
    DESCRIPTION:
    
          This function writes a block of data to the  indicated  file  from
       memory at the specified address. Data is written in  either  TEXT  or
       BINARY mode, depending on how the  file  was  opened.  If  the  value
       returned is less than the value of the "size" parameter,  some  error
       condition has occured (Such as disk full).
    
    
    EXAMPLES:
    
        if(fwrite(buffer, 100, fp) < 100)
            abort("File write error\n");

    GETC                                                               GETC
    
    
    
    PROTOTYPE:
    
        int getc(FILE *fp)
    
    
    ARGUMENTS:
    
        fp      - File pointer to an input file
    
    
    RETURN VALUE:
    
        Value of a character read from the file (0-255)
        EOF (-1) if end of file or an error condition occurs
    
    
    DESCRIPTION:
    
          This function reads a single character from  an  input  file,  and
       returns it as a positive value in the range of 0 to 255.  A  full  16
       bit value is returned, allowing the  end  of  file  condition  to  be
       distinct from the character value 255.
    
    
    EXAMPLES:
    
        if((c = getc(input_file)) == EOF)
            abort("End of file encountered\n");

    GETCHAR                                                         GETCHAR
    
    
    
    PROTOTYPE:
    
        int getchar()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        Value of a character read (0-255)
        EOF (-1) if end of file or an error condition occurs
    
    
    DESCRIPTION:
    
          This function reads a single character from the  "standard  input"
       file, and returns it as a positive value in the range of 0 to 255.  A
       full 16 bit value is returned, allowing the end of file condition  to
       be distinct from the character value 255.
    
    
    EXAMPLES:
    
        if((c = getchar()) == EOF)
            abort("End of file on TTY input\n");

    GETS                                                               GETS
    
    
    
    PROTOTYPE:
    
        char *gets(char *buffer)
    
    
    ARGUMENTS:
    
        buffer  - Pointer to string to receive line
    
    
    RETURN VALUE:
    
        Pointer to "buffer", or 0 if end of file
    
    
    DESCRIPTION:
    
          The "gets" function reads characters  from  the  "standard  input"
       input file, and places them in the character buffer until one of  two
       things happens:
    
          1) A NEWLINE character is encountered.
    
          2) The END of the file is encountered.
    
          The string is terminated with the standard NUL '\0' character. The
       trailing NEWLINE '\n' character is NOT included in the output buffer.
    
    
    EXAMPLES:
    
        puts("Enter input>");
        gets(input_line);

    GETDIR                                                           GETDIR
    
    
    
    PROTOTYPE:
    
        int getdir(char pathname[])
    
    
    ARGUMENTS:
    
        pathname- Address of string to receive directory path
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          This function retreives from the system the name of the  "current"
       directory path.
    
          The "pathname" string must be long  enough  to  hold  the  largest
       pathname supported by the system, as  indicated  by  the  "PATH_SIZE"
       definition in the "file.h" header file.
    
    
    EXAMPLES:
    
        getdir(&current_dir);

    GETENV                                                           GETENV
    
    
    
    PROTOTYPE:
    
        int getenv(char *ename, char *dest)
    
    
    ARGUMENTS:
    
        ename   - String containing name of environment variable
        dest    - Buffer to receive variable string value
    
    
    RETURN VALUE:
    
        1 if environment variable was found, 0 if not.
    
    
    DESCRIPTION:
    
          The GETENV function gets the value of a variable in  the  programs
       environment, and returns it as a string. If the environment  variable
       is not found, zero is returned, and the destination buffer is set  to
       a null (zero length) string.
    
          Use of this  function  allows  a  programs  fixed  parameters  and
       options to be specified once in environment variables, which may then
       be extracted by the program, eliminating the need  to  specify  those
       values every time the program is executed.
    
          When operating  MICRO-C  under  operating  systems  which  do  not
       support environment variables, this function will not be available.
    
    
    EXAMPLES:
    
        if(!getenv("COMSPEC", command))
            abort("No command processor defined\n");

    IN                                                                   IN
    
    
    
    PROTOTYPE:
    
        int in(unsigned port)
    
    
    ARGUMENTS:
    
        port    - I/O port address
    
    
    RETURN VALUE:
    
        The 8 bit value read from the given I/O port address
    
    
    DESCRIPTION:
    
          The "in" function reads and returns a byte (8 bits)  from  an  I/O
       port as an integer value between 0 and 255.
    
          The valid range of values for "port" depends on  the  I/O  address
       space of the processor.
    
          This function is not provided for processors which do not  support
       a separate I/O address space.
    
    
    EXAMPLES:
    
        while(in(0));   /* Wait for flag to clear */

    INW                                                                 INW
    
    
    
    PROTOTYPE:
    
        int inw(unsigned port)
    
    
    ARGUMENTS:
    
        port    - I/O port address
    
    
    RETURN VALUE:
    
        The 16 bit value read from the given I/O port address
    
    
    DESCRIPTION:
    
          The "inw" function reads and returns a word (16 bits) from an  I/O
       port as an integer value between 0 and 65535 (-1).
    
          The valid range of values for "port" depends on  the  I/O  address
       space of the processor.
    
          This function is not provided for processors which do not  support
       a separate I/O address space.
    
    
    EXAMPLES:
    
        var = inw(0);

    ISASCII                                                         ISASCII
    
    
    
    PROTOTYPE:
    
        int isascii(int c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is an ASCII character
        0 if 'c' is not an ASCII character
    
    
    DESCRIPTION:
    
          Returns TRUE (1) if the passed character  'c'  is  a  valid  ASCII
       character (0x00-0xFF), otherwise FALSE (0) is returned.
    
    
    EXAMPLES:
    
        if(!isascii(*ptr))
            abort("Invalid character data");

    ISALNUM                                                         ISALNUM
    
    
    
    PROTOTYPE:
    
        int isalnum(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is alphabetic or numeric
        0 if 'c' is not alphabetic or numeric
    
    
    DESCRIPTION:
    
          Returns  TRUE  (1)  if  the  passed  character  'c'  is  an  ASCII
       alphabetic letter in either upper or  lower  case  or  if  'c'  is  a
       numeric digit, otherwise FALSE (0) is returned.
    
    
    EXAMPLES:
    
        while(isalnum(*ptr))        /* Copy over symbol name */
            *name++ = *ptr++;

    ISALPHA                                                         ISALPHA
    
    
    
    PROTOTYPE:
    
        int isalpha(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is alphabetic
        0 if 'c' is not alphabetic
    
    
    DESCRIPTION:
    
          Returns  TRUE  (1)  if  the  passed  character  'c'  is  an  ASCII
       alphabetic letter in either upper or lower case, otherwise FALSE  (0)
       is returned.
    
    
    EXAMPLES:
    
        flag = isalpha(input_char);

    ISCNTRL                                                         ISCNTRL
    
    
    
    PROTOTYPE:
    
        int iscntrl(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is a "control" character
        0 if 'c' is not a "control" character
    
    
    DESCRIPTION:
    
          Returns TRUE (1) is the passed character 'c' is an ASCII "control"
       character (0x00-0x1F or 0x7F), otherwise FALSE (0) is returned.
    
    
    EXAMPLES:
    
        putc(iscntrl(c) ? '.' : c, stdout); /* Display controls as '.' */

    ISDIGIT                                                         ISDIGIT
    
    
    
    PROTOTYPE:
    
        int isdigit(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is numeric
        0 if 'c' is not numeric
    
    
    DESCRIPTION:
    
          Returns TRUE (1) is the passed character 'c'  is  an  ASCII  digit
       ('0'-'9'), otherwise FALSE (0) is returned.
    
    
    EXAMPLES:
    
        value = 0;
        while(isdigit(*ptr))
            value = (value * 10) + (*ptr++ - '0');

    ISGRAPH                                                         ISGRAPH
    
    
    
    PROTOTYPE:
    
        int isgraph(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is a non-space printable character
        0 if 'c' is a space or not printable
    
    
    DESCRIPTION:
    
          Returns TRUE (1) if the passed character 'c' is a printable  ASCII
       character other than  a  space  character,  otherwise  FALSE  (0)  is
       returned.
    
    
    EXAMPLES:
    
        putc(isgraph(c) ? c : '.', stdout);

    ISLOWER                                                         ISLOWER
    
    
    
    PROTOTYPE:
    
        int islower(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is lower case alphabetic
        0 if 'c' is not lower case alphabetic
    
    
    DESCRIPTION:
    
          Returns  TRUE  (1)  if  the  passed  character  'c'  is  an  ASCII
       alphabetic letter of lower case, otherwise FALSE (0) is returned.
    
    
    EXAMPLES:
    
        flag = islower(input_char);

    ISPRINT                                                         ISPRINT
    
    
    
    PROTOTYPE:
    
        int isprint(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is a printable character
        0 if 'c' is not printable
    
    
    DESCRIPTION:
    
          Returns TRUE (1) if the passed character 'c' is a printable  ASCII
       character (0x20-0xFE), otherwise FALSE (0) is returned.
    
    
    EXAMPLES:
    
        putc(isprint(c) ? c : '.', stdout);

    ISPUNCT                                                         ISPUNCT
    
    
    
    PROTOTYPE:
    
        int ispunct(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is a printable non-alphanumeric character
        0 if 'c' is not printable or alphanumeric
    
    
    DESCRIPTION:
    
          Returns TRUE (1) if the passed character 'c' is a printable  ASCII
       character which is not a letter of the alphabet or a  numeric  digit,
       otherwise FALSE (0) is returned.
    
    
    EXAMPLES:
    
        while(ispunct(*ptr))
            ++ptr;

    ISSPACE                                                         ISSPACE
    
    
    
    PROTOTYPE:
    
        int isspace(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is a space character (space, tab or newline)
        0 if 'c' is not a space character
    
    
    DESCRIPTION:
    
          Returns TRUE (1) if the passed character 'c' is one  of  a  space,
       tab or newline, otherwise FALSE (0) is returned.
    
    
    EXAMPLES:
    
        while(isspace(*ptr))
            ++ptr;

    ISUPPER                                                         ISUPPER
    
    
    
    PROTOTYPE:
    
        int isupper(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is upper case alphabetic
        0 if 'c' is not upper case alphabetic
    
    
    DESCRIPTION:
    
          Returns  TRUE  (1)  if  the  passed  character  'c'  is  an  ASCII
       alphabetic letter of upper case, otherwise FALSE (0) is returned.
    
    
    EXAMPLES:
    
        flag = isupper(input_char);

    ISXDIGIT                                                       ISXDIGIT
    
    
    
    PROTOTYPE:
    
        int isxdigit(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is a hexidecimal digit
        0 if 'c' is not a hexidecimal digit
    
    
    DESCRIPTION:
    
          Returns TRUE (1) is the passed character 'c'  is  an  valid  ASCII
       hexidecimal digit ('0'-'9', 'A'-'F', 'a'-'f'), otherwise FALSE (0) is
       returned.
    
    
    EXAMPLES:
    
        value = 0;
        while(isxdigit(*ptr))
            value = (value * 16) +
                (isdigit(*ptr) ? *ptr++ - '0' : toupper(*ptr++) - ('A'-10));

    ITOA                                                               ITOA
    
    
    
    PROTOTYPE:
    
        int itoa(unsigned value, char *string, int base)
    
    
    ARGUMENTS:
    
        value   - Value to convert to ASCII
        string  - String to receive ASCII representation
        base    - Numerical base in which to perform conversion
    
    
    RETURN VALUE:
    
        Number of digits written to the string buffer
    
    
    DESCRIPTION:
    
          This function accepts  a  binary  value,  and  converts  it  to  a
       printable ASCII number, using the specified numerical base.
    
          The numerical base used must be at least 2. If a base  of  greater
       than 36 is used, the symbolic "digits" for values  greater  than  'Z'
       are defined by the progrssion of the ASCII character set.
    
          The value is normally treated as an unsigned quantity, however  if
       the base is specified as a negative number, signed output (using '-')
       will be performed for negative values.
    
          The destination string buffer must be large  enough  to  hold  all
       digits resulting from the conversion plus a terminating '\0'.
    
    
    EXAMPLES:
    
        itoa(value, buffer, 10);    /* Get value in unsigned base 10 */
        itoa(value, buffer, -10);   /* Get value in signed base 10 */
        itoa(value, buffer, 16);    /* Get value in hexidecimal */
        itoa(value, buffer, 2);     /* Get value in binary */

    LGETC                                                             LGETC
    
    
    
    PROTOTYPE:
    
        int lgetc(HANDLE fh)
    
    
    ARGUMENTS:
    
        fh      - File handle for an input file
    
    
    RETURN VALUE:
    
        Value of a character read from the file (0-255)
        EOF (-1) if end of file or an error condition occurs
    
    
    DESCRIPTION:
    
          This function reads a single character from an  input  file  using
       LOW LEVEL (unbuffered) I/O, and returns it as a positive value in the
       range of 0 to 255. A full 16 bit value is returned, allowing the  end
       of file condition to be distinct from the character value 255.
    
    
    EXAMPLES:
    
        if((c = lgetc(input_file)) == EOF)
            abort("End of file encountered\n");

    LGETS                                                             LGETS
    
    
    
    PROTOTYPE:
    
        char *lgets(char *buffer, int size, HANDLE fh)
    
    
    ARGUMENTS:
    
        buffer  - Pointer to string to receive line
        size    - Maximum size of line to read
        fh      - File handle of an input file
    
    
    RETURN VALUE:
    
        Pointer to "buffer", or 0 if end of file
    
    
    DESCRIPTION:
    
          The "lgets" function reads characters  from  the  specified  input
       file using LOW  LEVEL  (unbuffered)  I/O,  and  places  them  in  the
       character buffer until one of three things happens:
    
          1) A NEWLINE character is encountered.
    
          2) The END of the file is encountered.
    
          3) The limit of "size" characters are read.
    
          The string is terminated with the standard  NULL  (00)  character.
       The trailing NEWLINE '\n' character is NOT  included  in  the  output
       buffer.
    
    
    EXAMPLES:
    
        lgets(input_line, 80, L_stdin);

    LONGJMP                                                         LONGJMP
    
    
    
    PROTOTYPE:
    
        longjmp(int savenv[3], int rvalue)
    
    
    ARGUMENTS:
    
        savenv  - Save area for program context
        rvalue  - Value to be returned by "setjmp"
    
    
    RETURN VALUE:
    
        N/A - Function never returns
    
    
    DESCRIPTION:
    
          The  "longjmp"  function  causes  execution  to  transfer  to  the
       "setjmp" call which  set  up  the  "savenv"  variable.  The  "setjmp"
       function will appear to return the value of "rvalue".
    
          NOTE-1: "longjmp" may  only  be  used  from  within  the  function
       calling "setjmp" or a function which has been called  "beneath"  that
       function. IT MUST NOT BE USED AFTER THE FUNCTION CALLING "SETJMP" HAS
       TERMINATED.
    
          NOTE-2: If "rvalue" is zero, the function  calling  "setjmp"  will
       assume that it is returning from initialization. Unless you want this
       unusual behavior, you should not pass  a  return  value  of  zero  to
       "longjmp".
    
          See also SETJMP.
    
    
    EXAMPLES:
    
        if(getc(stdin) == ('C'-'@'))    /* If Control-C entered... */
            longjmp(savearea, 1);       /* Return to main function */

    LONGMATH                                                       LONGMATH
    
    
    
    PROTOTYPES:
    
        int longadd(char *num1, char *num2);
        int longsub(char *num1, char *num2);
        longmul(char *num1, char *num2);
        longdiv(char *num1, char *num2);
        int longshr(char *num1);
        int longshl(char *num1);
        longcpy(char *num1, char *num2);
        longset(char *num1, unsigned value);
        int longtst(char *num1);
        int longcmp(char *num1, char *num2);
        extern char Longreg[];
    
    ARGUMENTS:
    
        num1    - First LONG operand, receives result if generated
        num2    - Second LONG operand, is not altered
        value   - 16 bit value to initialize LONG number with
    
    
    RETURN VALUE:
    
        longadd - 0 = Ok, 1 = addition overflowed
        longsub - 0 = Ok, 1 = subtraction underflowed
        longshr - Carry out of shift (1/0)
        longshl - Carry out of shift (1/0)
        longtst - 0 = Number is zero, !0 = Number is not zero
        longcmp - 0 = (num1 == num2), 1 = (num1 > num2), -1 = (num1 < num2)
    
    
    DESCRIPTION:
    
          This set of functions performs basic arithmetic functions on  LONG
       numbers:
    
        longadd(num1, num2)     ->  num1 += num2
        longsub(num1, num2)     ->  num1 -= num2
        longmul(num1, num2)     ->  num1 *= num2 , Longreg = num1 * num2
        longdiv(num1, num2)     ->  num1 /= num2 , Longreg = num1 % num2
        longshr(num1)           ->  num1 >>= 1
        longshl(num1)           ->  num1 <<= 1
        longcpy(num1, num2)     ->  num1 = num2
        longset(num1, value)    ->  num1 = (long) value
        longtst(num1)           ->  Test (num1 != 0)
        longcmp(num1, num2)     ->  Compare num1 and num2
    
          As shipped, a LONG number is 32 bits (4 bytes)  in  size,  however
       this can be changed by altering the LONGMATH.ASM in the library.
    
          For a complete example of using  these  functions,  refer  to  the
       LONGCALC.C example program included with the package.

    LPRINTF                                                         LPRINTF
    
    
    
    PROTOTYPE:
    
        register lprintf(int handle, char *format, arg, ...)
    
    
    ARGUMENTS:
    
        handle  - DOS file handle of output file
        format  - Pointer to format string
        arg     - Argument as determined by format string
        ...     - Additional arguments may be required
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This routine performs a formatted print to  a  file  specified  by
       'fh', using LOW LEVEL (unbuffered) I/O.
    
          The 'format' string is written to  the  file  with  the  arguments
       substituted for special "conversion characters".  See  "fprintf"  for
       more information on format strings and conversions.
    
          NOTE: This function uses a variable number of arguments, and  must
       be declared as "register" (See "stdio.h").
    
    
    EXAMPLES:
    
        lprintf(fh, "Total errors=%u", error_count);

    LPUTC                                                             LPUTC
    
    
    
    PROTOTYPE:
    
        lputc(char c, HANDLE fh)
    
    
    ARGUMENTS:
    
        c       - Any character value
        fh      - File handle of an output file
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DECRIPTION:
    
          This function writes the character 'c' to the  file  indicated  by
       'fh' using LOW LEVEL (unbuffered) I/O. The "newline"  (\n)  character
       will be translated into whatever character(s)  are  required  by  the
       operating system to separate records in the file.
    
    
    EXAMPLES:
    
        lputc('*', fh);
        lputc('\n', L_stderr);

    LPUTS                                                             LPUTS
    
    
    
    PROTOTYPE:
    
        lputs(char *string, HANDLE fh)
    
    
    ARGUMENTS:
    
        string  - Pointer to a character string
        fh      - File handle of an output file
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          The "lputs" function writes the specified string to the  indicated
       output file using LOW LEVEL (unbuffered) I/O.  The  zero  terminating
       the string is NOT written.
    
    
    EXAMPLES:
    
        lputs("Text message", output_fh);

    LREWIND                                                         LREWIND
    
    
    
    PROTOTYPE:
    
        int lrewind(HANDLE fh)
    
    
    ARGUMENTS:
    
        fh      - File handle of an open file
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          This function resets the operating system internal file handle  so
       than any subsequent read or writes will be at the  beginning  of  the
       file. For use with LOW LEVEL (unbuffered) file I/O only.
    
    
    EXAMPLES:
    
        lrewind(input_fh);

    LSCANF                                                           LSCANF
    
    
    
    PROTOTYPE:
    
        register int lscanf(int fh, char *format, &arg, ...)
    
    
    ARGUMENTS:
    
        fh      - DOS file handle of input file
        format  - Pointer to format string
        arg     - Argument as determined by format string
        ...     - Additional arguments may be required
    
    
    RETURN VALUE:
    
        The number of successful matches
        EOF (-1) if end of file or an error condition occurs
    
    
    DESCRIPTION:
    
          This routine reads a line from the specified file using LOW  LEVEL
       (unbuffered) I/O, and scans it for specific  values  which  are  then
       assigned to the  passed  argument  addresses.  The  types  of  values
       scanned are determined by special "conversion characters" within  the
       "format" string.
    
          See "fscanf" for more information on format strings.
    
          NOTE: This function uses a variable number of arguments, and  must
       be declared as "register".
    
    
    EXAMPLES:
    
        if(lscanf(infile,"%s %s %u", first_name, last_name, &age) != 3)
            abort("Error in user record\n");

    LSEARCH                                                         LSEARCH
    
    
    
    PROTOTYPE:
    
        char *lsearch(char *k, char *t, unsigned e, unsigned s, int (*f)())
    
    
    ARGUMENTS:
    
        k   - Key to search for
        t   - Table to search
        e   - Number on entries in the table
        s   - Size of each entry
        f   - Pointer to function performing compare
    
    
    RETURN VALUE:
    
        Address of found record, or zero (0) if no match
    
    
    DESCRIPTION:
    
          Performs a linear search of the specified table, looking  for  the
       given key. Since this is a linear search, the table  may  be  in  any
       order.
    
          Any fixed format table can be used. The key and a pointer to  each
       entry to test are passed to the user supplied compare function, which
       must return 0 if equal, <0 if the key (first arg) is  less  than  the
       table entry, or >0 if the key is larger than the table entry.
    
    
    EXAMPLES:
    
        #include <stdio.h>
        int table[] = { 453, 762, 132, 982, 281, 185, 300, 737 };
        int test(int *a, int *b) { return *a - *b; }
        main(argc, char *argv[])
        {
            int key;
            key = atoi(argv[1]);
            printf("%04x", lsearch(&key, table, 8, sizeof(int), &test));
        }

    LSEEK                                                             LSEEK
    
    
    
    PROTOTYPE:
    
        (1) int lseek(HANDLE fh, int h_offset, unsigned l_offset, int mode)
        (2) int lseek(HANDLE fh, int offset, mode)
    
    
    ARGUMENTS:
    
        fh  - File handle of an open file
        h_offset- Highest 16 bits of offset value
        l_offset- Lowest 16 bits of offset value
        offset  - 16 bit offset value
        mode    - Type of seek
                    0 = Absolute from start of file
                    1 = Signed offset from current position
                    2 = Signed offset from end of file
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          This function positions the operating system internal pointer into
       a file so that any read or write will take  place  at  the  specified
       position in the file.
    
          Most operating systems which support files of > 64K bytes in  size
       will support form (1) of the function, using both high and low offset
       values.
    
          Smaller operating  systems  may  only  support  form  (2)  of  the
       function, allowing seeking of only +/- 32K bytes.
    
          Also, some implementations may not support  all  "modes",  or  may
       only allow unsigned (positive) offsets.
    
          For use with LOW LEVEL (unbuffered I/O only).
    
    
    EXAMPLES:
    
        lseek(input_fh, 0, 2);  /* Advance to end of file */

    LTELL                                                             LTELL
    
    
    
    PROTOTYPE:
    
        (1) int ltell(HANDLE fh, int &h_offset, unsigned &l_offset)
        (2) int ltell(HANDLE fh, int &offset)
    
    
    ARGUMENTS:
    
        fh      - File handle of an open file
        h_offset- Address of int to receive high word of offset
        l_offset- Address of int to receive low word of offset
        offset  - Address of int to receive offset
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          This function gets the current read/write position within a  file.
       The position returned indicates the absolute character (byte)  offset
       from the start of the file where the next read  or  write  will  take
       place.
    
          Most operating systems which support files of > 64K bytes in  size
       will support form (1) of the function, returning both  high  and  low
       offset values.
    
          Smaller operating  systems  may  only  support  form  (2)  of  the
       function,  allowing  access  to  only  the  first   65535   character
       positions.
    
          For use with LOW LEVEL (unbuffered I/O only).
    
    
    EXAMPLES:
    
        ltell(fp, &oldh, &oldl);    /* Save file position */
            . . .                   /* Perform some operations on the file */
        lseek(fp, oldh, oldl, 0);   /* Return to previous position */

    MALLOC                                                           MALLOC
    
    
    
    PROTOTYPE:
    
        char *malloc(int size)
    
    
    ARGUMENTS:
    
        size    - Size of memory block to allocate (in bytes).
    
    
    RETURN VALUE:
    
        0       - Memory allocation failed
        !0      - Pointer to allocated memory block
    
    
    DESCRIPTION:
    
          The "malloc" function allocates a block of memory of the specified
       size from the heap, and returns a pointer to it. The allocated memory
       will have undefined content until written by the user  program.  This
       memory will remain allocated until it is explicitly released with the
       "free" function.
    
    
    EXAMPLES:
    
        if(!(ptr = malloc(BUFSIZ)))     /* Allocate a temporary buffer */
            abort("Not enough memory");
        do {                            /* Copy the file over */
            size = fread(ptr, BUFSIZ, in_fp);
            fwrite(ptr, size, out_fp); }
        while(size == BUFSIZ);
        free(ptr);                      /* Release temporary buffer */

    MAX                                                                 MAX
    
    
    
    PROTOTYPE:
    
        int max(int value1, int value2)
    
    
    ARGUMENTS:
    
        value1  - Any integer value
        value2  - Any integer value
    
    
    RETURN VALUE:
    
        The greater of "value1" or "value2"
    
    
    DESCRIPTION:
    
          The "max" function returns the higher of its two argument values.
    
    
    EXAMPLES:
    
        biggest = max(a, b);

    MEMCHR                                                           MEMCHR
    
    
    
    PROTOTYPE:
    
        char *memchr(char *mem, char c, unsigned size)
    
    
    ARGUMENTS:
    
        mem     - Block of memory to search
        c       - Character to look for
        size    - Size of block
    
    
    RETURN VALUE:
    
        Pointer to first character found or zero (0) if not found
    
    
    DESCRIPTION:
    
          This function searches the specified block of memory, looking  for
       the given character.
    
          If the character is located within the block,  a  pointer  to  the
       character is returned.
    
          If the character is not found before the specified  "size"  number
       of bytes have been examined, a zero is returned.
    
    
    EXAMPLES:
    
        if(ptr = memchr(block, '*', sizeof(block))
            printf("Block contains '*' at address: %04x\n", ptr);

    MEMCMP                                                           MEMCMP
    
    
    
    PROTOTYPE:
    
        int memcmp(unsigned char *b1, unsigned char *b2, unsigned size)
    
    
    ARGUMENTS:
    
        b1      - First memory block to compare
        b2      - Second memory block to compare
        size    - Size of blocks
    
    
    RETURN VALUE:
    
        0   - Blocks match exactly
        1   - Block1 is greater than string2
        -1  - Block2 is greater than string1
    
    
    DESCRIPTION:
    
          This  function  compares  two  blocks  of  memory   character   by
       character. If the two blocks are identical for the  specified  "size"
       number of bytes, a zero (0)  is  returned.  If  the  first  block  is
       greater than the second (as far as ASCII is concerned), a one (1)  is
       returned. If the second block is greater,  a  negative  one  (-1)  is
       returned.
    
    
    EXAMPLES:
    
        if(memcmp(old_block, new_block, sizeof(old_block))
            printf("New copy of block has been modified");

    MEMCPY                                                           MEMCPY
    
    
    
    PROTOTYPE:
    
        memcpy(char *dest, char *source, unsigned size)
    
    
    ARGUMENTS:
    
        dest    - Pointer to the destination
        source  - Pointer to the souce
        size    - Number of bytes to copy
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "memcpy" function will copy the specified number of bytes from
       the source to the destination. If the source and  destination  blocks
       overlap, the function may not copy the entire block correctly.
    
    
    EXAMPLES:
    
        memcpy(buffer1, buffer2, 256);

    MEMMOVE                                                         MEMMOVE
    
    
    
    PROTOTYPE:
    
        memmove(char *dest, char *source, unsigned size)
    
    
    ARGUMENTS:
    
        dest    - Pointer to the destination
        source  - Pointer to the souce
        size    - Number of bytes to copy
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function is similar to "memcpy", with the exception  that  it
       will copy overlapping blocks  of  memory  correctly.  It  is  however
       slightly larger than memcpy().
    
    
    EXAMPLES:
    
        memmove(buffer1, buffer2, 256);

    MEMSET                                                           MEMSET
    
    
    
    PROTOTYPE:
    
        memset(char *block, char value, unsigned size)
    
    
    ARGUMENTS:
    
        block   - Pointer to a block of memory
        value   - Value to initialize memory with
        size    - Number of bytes to initialize
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          Sets a block of memory  beginning  at  the  pointer  "block",  for
       "size" bytes to the byte value "value".
    
    
    EXAMPLES:
    
        memset(buffer, 0, 100);

    MIN                                                                 MIN
    
    
    
    PROTOTYPE:
    
        int min(int value1, int value2)
    
    
    ARGUMENTS:
    
        value1  - Any integer value
        value2  - Any integer value
    
    
    RETURN VALUE:
    
        The smaller of "value1" or "value2"
    
    
    DESCRIPTION:
    
          The "min" function returns the lower of its two argument values.
    
    
    EXAMPLES:
    
        least = min(a, b);

    MKDIR                                                             MKDIR
    
    
    
    PROTOTYPE:
    
        int mkdir(char *pathname)
    
    
    ARGUMENTS:
    
        pathname- Name of directory to create
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          The "mkdir" function create a new directory on the disk under  the
       specified path name.
    
    
    EXAMPLES:
    
        mkdir("subdir");

    NARGS                                                             NARGS
    
    
    
    PROTOTYPE:
    
        int nargs()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        The number of arguments passed to the calling function
    
    
    DESCRIPTION:
    
          Returns the number of arguments passed to a "register" function.
    
          NOTE: When  calling  a  "register"  function,  MICRO-C  loads  the
       accumulator with the number of arguments just prior  to  calling  the
       function. This "nargs" routine is  simply  a  null  definition  which
       returns with the same value in the accumulator as was there  when  it
       was called. Therefore "nargs" MUST BE  THE  FIRST  ARITHMETIC  ENTITY
       EVALUATED WITHIN  THE  REGISTER  FUNCTION  or  the  contents  of  the
       accumulator will be lost. Some examples of "register" definitions and
       the use of "nargs" may be found in the library source code.
    
    
    EXAMPLES:
    
        first_arg = nargs() * 2 + &arguments;

    OPEN                                                               OPEN
    
    
    
    PROTOTYPE:
    
        HANDLE open(char *filename, int options)
    
    
    ARGUMENTS:
    
        filename- Name of the file to open
        options - Open options (defined in file.h)
    
    
    RETURN VALUE:
    
        File handle for the open file
        Zero (0) if file could not be opened
    
    
    DESCRIPTION:
    
          This function  open  a  file  for  direct  access  via  LOW  LEVEL
       (unbuffered) I/O.
    
    
    EXAMPLES:
    
        if(fh = open("data.img", F_READ)) {
            read(data_buf, 100, fh);
            close(fh); }
        else
            abort("Unable to read data file");

    OUT                                                                 OUT
    
    
    
    PROTOTYPE:
    
        out(unsigned port, int value)
    
    
    ARGUMENTS:
    
        port    - I/O port address
        value   - Value to write to I/O port
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "out" function writes a byte (8 bit) value to an I/O port.
    
          The valid range of values for "port" depends on  the  I/O  address
       space of the processor.
    
          This function is not provided for processors which do not  support
       a separate I/O address space.
    
    
    EXAMPLES:
    
        out(0, 0);      /* Output 0 to I/O port 0 */

    OUTW                                                               OUTW
    
    
    
    PROTOTYPE:
    
        outw(unsigned port, int value)
    
    
    ARGUMENTS:
    
        port    - I/O port address
        value   - Value to write to I/O port
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "outw" function writes a word (16 bit) value to an I/O port.
    
          The valid range of values for "port" depends on  the  I/O  address
       space of the processor.
    
          This function is not provided for processors which do not  support
       a separate I/O address space.
    
    
    EXAMPLES:
    
        outw(0, 0);     /* Write 0 to I/O ports 0 and 1 */

    PEEK                                                               PEEK
    
    
    
    PROTOTYPE:
    
        (1) int peek(unsigned address)
        (2) int peek(unsigned h_addr, unsigned l_addr)
        (3) int peek(unsigned segment, unsigned offset)
    
    
    ARGUMENTS:
    
        segment - Memory segment
        offset  - Offset into segment
        h_addr  - High word of memory address
        l_addr  - Low word of memory address
        address - 16 bit memory address
    
    
    RETURN VALUE:
    
        The 8 bit value read from the given memory address
    
    
    DESCRIPTION:
    
          The "peek" function reads and returns a byte (8 bits) from  memory
       as an integer value between 0 and 255.
    
          Processors such as the 8080 or 6809 which address 64K of memory or
       less use form (1) of the function.
    
          Non-segmented processors addressing more  than  64K  such  as  the
       68000 use form (2) of the function.
    
          Processors employing a "segmented" architecture such as  the  8086
       use form (3) of the function.
    
    
    EXAMPLES:
    
        while(peek(0)); /* Wait for flag to clear */

    PEEKW                                                             PEEKW
    
    
    
    PROTOTYPE:
    
        (1) int peekw(unsigned address)
        (2) int peekw(unsigned h_addr, unsigned l_addr)
        (3) int peekw(unsigned segment, unsigned offset)
    
    
    ARGUMENTS:
    
        segment - Memory segment
        offset  - Offset into segment
        h_addr  - High word of memory address
        l_addr  - Low word of memory address
        address - 16 bit memory address
    
    
    RETURN VALUE:
    
        The 16 bit value read from the given memory address
    
    
    DESCRIPTION:
    
          The "peekw" function reads and  returns  a  word  (16  bits)  from
       memory as an integer value between 0 and 65535 (-1).
    
          Processors such as the 8080 or 6809 which address 64K of memory or
       less use form (1) of the function.
    
          Non-segmented processors addressing more  than  64K  such  as  the
       68000 use form (2) of the function.
    
          Processors employing a "segmented" architecture such as  the  8086
       use form (3) of the function.
    
    
    EXAMPLES:
    
        var = peekw(0));

    POKE                                                               POKE
    
    
    
    PROTOTYPE:
    
        (1) poke(unsigned address, int value)
        (2) poke(unsigned h_addr, unsigned l_addr, int value)
        (3) poke(unsigned segment, unsigned offset, int value)
    
    
    ARGUMENTS:
    
        segment - Memory segment
        offset  - Offset into segment
        h_addr  - High word of memory address
        l_addr  - Low word of memory address
        address - 16 bit memory address
        value   - Value to be written to memory
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "poke" function writes a byte (8 bit) value to memory.
    
          Processors such as the 8080 or 6809 which address 64K of memory or
       less use form (1) of the function.
    
          Non-segmented processors addressing more  than  64K  such  as  the
       68000 use form (2) of the function.
    
          Processors employing a "segmented" architecture such as  the  8086
       use form (3) of the function.
    
    
    EXAMPLES:
    
        poke(0, 0);     /* Write 0 to location 0 */

    POKEW                                                             POKEW
    
    
    
    PROTOTYPE:
    
        (1) pokew(unsigned address, int value)
        (2) pokew(unsigned h_addr, unsigned l_addr, int value)
        (3) pokew(unsigned segment, unsigned offset, int value)
    
    
    ARGUMENTS:
    
        segment - Memory segment
        offset  - Offset into segment
        h_addr  - High word of memory address
        l_addr  - Low word of memory address
        address - 16 bit memory address
        value   - Value to be written to memory
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "pokew" function writes a word (16 bit) value to memory.
    
          Processors such as the 8080 or 6809 which address 64K of memory or
       less use form (1) of the function.
    
          Non-segmented processors addressing more  than  64K  such  as  the
       68000 use form (2) of the function.
    
          Processors employing a "segmented" architecture such as  the  8086
       use form (3) of the function.
    
    
    EXAMPLES:
    
        pokew(0, 0);    /* Write 0 to locations 0 and 1 */

    PRINTF                                                           PRINTF
    
    
    
    PROTOTYPE:
    
        register printf(char *format, arg, ...)
    
    
    ARGUMENTS:
    
        format  - Pointer to format string
        arg     - Argument as determined by format string
        ...     - Additional arguments may be required
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "printf" routine performs a formatted print  to  the  standard
       output device  (usually  system  console).  The  "format"  string  is
       written  with  the  arguments  substituted  for  special  "conversion
       characters".
    
          See "fprintf" for more information on format strings.
    
          NOTE: This function uses a variable number of arguments, and  must
       be declared as "register" (See "stdio.h").
    
    
    EXAMPLES:
    
        printf("Hello world!!!\n");
        printf("File '%s', has %u lines\n", filename, num_lines);

    PUTC                                                               PUTC
    
    
    
    PROTOTYPE:
    
        putc(char c, FILE *fp)
    
    
    ARGUMENTS:
    
        c       - Any character value
        fp      - File pointer to an output file
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DECRIPTION:
    
          This function writes the character 'c' to the  file  indicated  by
       the file pointer 'fp'.
    
    
    EXAMPLES:
    
        putc('*', fp);
        putc('\n', stderr);

    PUTCHAR                                                         PUTCHAR
    
    
    
    PROTOTYPE:
    
        putchar(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DECRIPTION:
    
          This function writes the character 'c' to  the  "standard  output"
       file.  This  is  normall  the  user  tty,  unless  output  has   been
       re-directed by the operating system.
    
    
    EXAMPLES:
    
        putchar('*');
        putchar('\n');

    PUTS                                                               PUTS
    
    
    
    PROTOTYPE:
    
        puts(char *string)
    
    
    ARGUMENTS:
    
        string  - Pointer to a character string
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          The "puts" function writes the specified string to  the  "standard
       output" file, followed by a NEWLINE character. The  zero  terminating
       the string is NOT written.
    
    
    EXAMPLES:
    
        puts("Enter input>");
        gets(input_line);

    QSORT                                                             QSORT
    
    
    
    PROTOTYPE:
    
        qsort(char *base, unsigned e, unsigned s, int (*f)())
    
    
    ARGUMENTS:
    
        base    - Beginning address of memory structure
        e       - Number of elements in structure
        s       - Size of each element
        f       - Pointer to compare function
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          Sorts  the  specified  table  in  memory  using  the   "quicksort"
       algorithm.
    
          Any fixed format table can be used. Pointers  to  elements  to  be
       sorted are passed to the user supplied compare function,  which  must
       return 0 if equal, <0 if the first argument is less than the  second,
       or or >0 if the first argument is larger than the second.
    
    
    EXAMPLES:
    
        #include <stdio.h>
        #define NELEM(x) ( sizeof(x) / sizeof(x[]) )
        char t[7][4] = { "foo","abc","car","abe","zax","bar","fun" };
        extern int strcmp();
        main()
        {
            int i;
            qsort(t, NELEM(t), sizeof(t[]), &strcmp);
            for(i=0; i < NELEM(t); ++i)
                printf("%s\n", t[i]);
        }

    RAND                                                               RAND
    
    
    
    PROTOTYPE:
    
        unsigned rand(unsigned limit)
    
    
    ARGUMENTS:
    
        limit   - Maximum value to return
    
    
    RETURN VALUE:
    
        A pseudo-random number in the range of 0 to (limit-1)
    
    
    DESCRIPTION:
    
          The "rand" function calculates the next value of  a  pseudo-random
       sequence, based on a 16 bit unsigned "seed" value, which it maintains
       in the global variable "RAND_SEED". The new value is  stored  as  the
       new seed value, and is then divided  by  the  "limit"  parameter,  to
       obtain the remainder, which is returned. This  results  in  a  random
       number in the range of zero (0) to (limit - 1).
    
          Any  particular  sequence  may  be  repeated,  by   reseting   the
       "RAND_SEED" value.
    
    
    EXAMPLES:
    
        value = rand(52);

    READ                                                               READ
    
    
    
    PROTOTYPE:
    
        int read(char *buffer, int size, HANDLE fh)
    
    
    ARGUMENTS:
    
        buffer  - Pointer to buffer to receive data
        size    - Number of bytes to read
        fh      - File handle of an input file
    
    
    RETURN VALUE:
    
        Number of bytes read from file
    
    
    DESCRIPTION:
    
          This function reads a block of data from a file  using  LOW  LEVEL
       (unbuffered) I/O, and places it in memory at the address of "buffer".
       Data is read in "raw"  form,  with  no  interpretation  of  "newline"
       characters etc. If the number of bytes  returned  is  less  than  the
       number of bytes requested, either the end of the file was encountered
       or an error condition occured (in which case the value will be zero).
    
    
    EXAMPLES:
    
        read(block, 512, input_fh);

    RENAME                                                           RENAME
    
    
    
    PROTOTYPE:
    
        int rename(char *pathname, char *newname)
    
    
    ARGUMENTS:
    
        pathname- Name of file to rename
        newname - New name for file
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          This function changes the name of an existing file  to  the  ASCII
       string specified by newname.
    
    
    EXAMPLES:
    
        rename("output.dat", "output.bak");

    REWIND                                                           REWIND
    
    
    
    PROTOTYPE:
    
        int rewind(FILE *fp)
    
    
    ARGUMENTS:
    
        fp      - File pointer to an open file
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          This function resets the operating system internal file pointer so
       than any subsequent read or writes will be at the  beginning  of  the
       file.
    
    
    EXAMPLES:
    
        rewind(input_file);

    RMDIR                                                             RMDIR
    
    
    
    PROTOTYPE:
    
        int rmdir(char *pathname)
    
    
    ARGUMENTS:
    
        pathname- Name of directory to delete
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          This function removes a directory from the disk. On most  systems,
       the directory  must  be  empty  (contains  no  files)  otherwise  the
       function will fail.
    
    
    EXAMPLES:
    
        rmdir("subdir");

    SCANF                                                             SCANF
    
    
    
    PROTOTYPE:
    
        register int scanf(char *format, arg1, arg2, ...)
    
    
    ARGUMENTS:
    
        format  - Pointer to format string
        arg     - Argument as determined by format string
        ...     - Additional arguments may be required
    
    
    RETURN VALUE:
    
        The number of successful matches
        EOF (-1) if end of file or an error condition occurs
    
    
    DESCRIPTION:
    
          The "scanf" function reads and scans  a  line  from  the  standard
       input device (usually system console) for specific values. Values are
       read and assigned to  the  passed  argument  addresses  according  to
       special "conversion characters" in the "format" string.
    
          See "fscanf" for more information on format strings.
    
          NOTE: This function uses a variable number of arguments, and  must
       be declared as "register".
    
    
    EXAMPLES:
    
        do
            printf("Please enter your First & Last names, and your age?");
        while(scanf("%s %s %u", first_name, last_name, &age) != 3);

    SETBUF                                                           SETBUF
    
    
    
    PROTOTYPE:
    
        FILE *setbuf(FILE *fp, int size)
    
    
    ARGUMENTS:
    
        fp      - File pointer to an open file
        size    - Size of new I/O buffer
    
    
    RETURN VALUE:
    
        If successful, a new file pointer is returned, and the old one
        is released. On failure the old file pointer is returned.
    
    
    DESCRIPTION:
    
          The "setbuf" function will adjust the size of the buffer used  for
       I/O operations on the indicated open file.
    
          This is the ONLY way to set the buffer size for  the  "stdin"  and
       "stdout" streams. If you change the size of the "stdout" buffer,  you
       must remember to "fflush(stdout)" before terminating,  otherwise  the
       last buffer contents may not be written.
    
          For file opened by "fopen",  the  buffer  size  may  be  set  more
       efficently by setting the value of the external  variable  "IOB_size"
       prior to calling "fopen".
    
          If "setbuf" is unable to allocate space for  the  new  buffer,  it
       will return the old file pointer unchanged.
    
    
    EXAMPLES:
    
        stdout = setbuf(stdout, 512);   /* Set stdout to 512 byte buffer */

    SETJMP                                                           SETJMP
    
    
    
    PROTOTYPE:
    
        int setjmp(int savenv[3])
    
    
    ARGUMENTS:
    
        savenv  - Save area for program context
    
    
    RETURN VALUE:
    
        0 is returned when actually called
        Value passed to "longjmp" is returned otherwise
    
    
    DESCRIPTION:
    
          When called, the "setjmp" function stores  the  current  execution
       state of the program into the passed integer array, and  returns  the
       value zero.
    
          The "longjmp" function may then be used to return the  program  to
       the "setjmp" call. In this case, the value returned by "setjmp"  will
       be the value which was passed to "longjmp". This allows the  function
       containing "setjmp" to determine which call to  "longjmp"  transfered
       execution to it.
    
          See also LONGJMP.
    
    
    EXAMPLES:
    
        switch(setjmp(savearea)) {
            case 0 : printf("Longjmp has been set up"); break;
            case 1 : printf("Control-C Interrupt");     break;
            case 2 : printf("Reset command executed");  break;
            default: printf("Software error trap");     break; }

    SPRINTF                                                         SPRINTF
    
    
    
    PROTOTYPE:
    
        register sprintf(char *dest, char *format, arg, ...)
    
    
    ARGUMENTS:
    
        dest    - Pointer to destination string
        format  - Pointer to format string
        arg     - Argument as determined by format string
        ...     - Additional arguments may be required
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "sprintf" routine performs a formatted print to  a  string  in
       memory. The "format" string is written to the destination string with
       the arguments substituted for special "conversion characters".
    
          See "fprintf" for more information on format strings.
    
          NOTE: This function uses a variable number of arguments, and  must
       be declared as "register" (See "stdio.h").
    
    
    EXAMPLES:
    
        sprintf(header_file, "/lib/%s.h", header_name);

    SQRT                                                               SQRT
    
    
    
    PROTOTYPE:
    
        int sqrt(unsigned value)
    
    
    ARGUMENTS:
    
        value   - Number for which to calculate square root
    
    
    RETURN VALUE:
    
        The integer square root (rounded up) of the argument value
    
    
    DESCRIPTION:
    
          The  SQRT  function  returns  the  smallest  number   which   when
       multiplied by itself will give a number equal to or larger  that  the
       argument value.
    
    
    EXAMPLES:
    
    /*
     * Draw a circle about point (x, y) of radus (r)
     */
    circle(x, y, r)
        int x, y, r;
    {
        int i, j, k, rs, lj;
    
        rs = (lj = r)*r;
        for(i=0; i <= r; ++i) {
            j = k = sqrt(rs - (i*i));
            do {
                plot_xy(x+i, y+j);
                plot_xy(x+i, y-j);
                plot_xy(x-i, y+j);
                plot_xy(x-i, y-j); }
            while(++j < lj);
            lj = k; }
    }

    SSCANF                                                           SSCANF
    
    
    
    PROTOTYPE:
    
        register int sscanf(char *input, char *format, arg1, arg2, ...)
    
    
    ARGUMENTS:
    
        input   - Pointer to input string
        format  - Pointer to format string
        arg     - Argument as determined by format string
        ...     - Additional arguments may be required
    
    
    RETURN VALUE:
    
        The number of successful matches
    
    
    DESCRIPTION:
    
          The "sscanf" function  scans  a  string  in  memory  for  specific
       values. Values are read and assigned to the passed argument addresses
       according to special "conversion characters" in the "format" string.
    
          See "fscanf" for more information on format strings.
    
          NOTE: This function uses a variable number of arguments, and  must
       be declared as "register".
    
    
    EXAMPLES:
    
        sscanf(pathname,"/%s/%s", directory, filename);

    STRBEG                                                           STRBEG
    
    
    
    PROTOTYPE:
    
        int strbeg(char *string1, char *string2)
    
    
    ARGUMENTS:
    
        string1 - Pointer to character string to test
        string2 - Pointer to character string to check for
    
    
    RETURN VALUE:
    
        0   - String1 does not begin with string2
        1   - String1 begins with string2
    
    
    DECRIPTION:
    
          Tests the passed "string1" to determine if it begins with the same
       data as is contained within "string2".
    
    
    EXAMPLES:
    
        if(strbeg(command, "delete"))
            delete_file(&command[6]);

    STRCAT                                                           STRCAT
    
    
    
    PROTOTYPE:
    
        char *strcat(char *dest, *source)
    
    
    ARGUMENTS:
    
        dest    - Pointer to destination string
        source  - Pointer to source string
    
    
    RETURN VALUE:
    
        Pointer to zero terminating destination string
    
    
    DESCRIPTION:
    
          This function concatinates the source string onto the tail of  the
       destination string. The destination string must be  large  enough  to
       hold the entire contents of both strings.
    
    
    EXAMPLES:
    
        strcat(program_name, ".c");

    STRCHR                                                           STRCHR
    
    
    
    PROTOTYPE:
    
        char *strchr(char *string, char chr)
    
    
    ARGUMENTS:
    
        string  - Pointer to a character string
        chr     - Character to look for
    
    
    RETURN VALUE:
    
        Pointer to the first occurance of 'chr' in 'string'
        Zero (0) if character was not found
    
    
    DECRIPTION:
    
          Searches  the  passed  string  for  the  first  occurance  of  the
       specified character. If the character is  found,  a  pointer  to  its
       position in the string is returned. If the character is not found,  a
       null pointer is returned.
    
          The null (0) character is treated as valid data by this  function,
       thus:
          strchr(string, 0);
    
       would return the position of the null terminator of the string.
    
    
    EXAMPLES:
    
        comma = strchr(buffer, ',');

    STRCMP                                                           STRCMP
    
    
    
    PROTOTYPE:
    
        int strcmp(char *string1, char *string2)
    
    
    ARGUMENTS:
    
        string1 - Pointer to first string
        string2 - Pointer to second string
    
    
    RETURN VALUE:
    
        0   - Strings match exactly
        1   - String1 is greater than string2
        -1  - String2 is greater than string1
    
    
    DESCRIPTION:
    
          This function compares two strings character by character. If  the
       two strings are identical, a zero  (0)  is  returned.  If  the  first
       string is greater than the second (as far as ASCII is  concerned),  a
       one (1) is returned. If the second string is greater, a negative  one
       (-1) is returned.
    
    
    EXAMPLES:
    
        if(!strcmp(command, "quit"))
            exit(0);

    STRCPY                                                           STRCPY
    
    
    
    PROTOTYPE:
    
        char *strcpy(char *dest, char *source)
    
    
    ARGUMENTS:
    
        dest    - Pointer to destination string
        souce   - Pointer to source string
    
    
    RETURN VALUE:
    
        Pointer to zero terminating destination string
    
    
    DESCRIPTION:
    
          This function copies the source string to the destination  string.
       All data is copied up to and including the zero byte which terminates
       the string. The destination string must be large enough to  hold  the
       entire source.
    
    
    EXAMPLES:
    
        strcpy(filename, argv[1]);

    STRCSPN                                                         STRCSPN
    
    
    
    PROTOTYPE:
    
        int strcspn(char *string, char *set
    
    
    ARGUMENTS:
    
        string  - String to test
        set     - Set of characters to look for
    
    
    RETURN VALUE:
    
        Length of string segment containing chars NOT in set.
    
    
    DESCRIPTION:
    
          Scans a  string  for  an  "initial  segment"  not  containing  any
       characters from the specified set. The value returned is  the  number
       of characters at the beginning of the specified string which  do  not
       occur in the specified set.
    
    
    EXAMPLES:
    
        cmd_length = strcspn(command, " \t,.");

    STRDUP                                                           STRDUP
    
    
    
    PROTOTYPE:
    
        char *strdup(char *string)
    
    
    ARGUMENTS:
    
        string  - String to duplicate
    
    
    RETURN VALUE:
    
        Pointer to newly allocated character string
        Zero (0) of memory allocation failed
    
    
    DESCRIPTION:
    
          Allocates a buffer in memory (via malloc) long enough to hold  the
       specified string (complete with  '\0'  terminator),  and  copies  the
       string into it.
    
    
    EXAMPLES:
    
        ptr = strdup(command_line);     /* Copy because strtok modifies */
        ptr1 = strtok(ptr, " \t");
        while(ptr1) {
            process_token(ptr1);
            ptr1 = strtok(0, " \t"); }
        free(ptr);

    STRICMP                                                         STRICMP
    
    
    
    PROTOTYPE:
    
        int stricmp(char *string1, char *string2)
    
    
    ARGUMENTS:
    
        string1 - Pointer to first string
        string2 - Pointer to second string
    
    
    RETURN VALUE:
    
        0   - Strings match exactly
        1   - String1 is greater than string2
        -1  - String2 is greater than string1
    
    
    DESCRIPTION:
    
          This function compares two strings character by character  without
       case sensitivity. If the two strings are identical (except for case),
       a zero (0) is returned. If the  first  string  is  greater  than  the
       second (as far as ASCII is concerned), a one (1) is returned. If  the
       second string is greater, a negative one (-1) is returned.
    
    
    EXAMPLES:
    
        if(!stricmp(command, "quit"))
            exit(0);

    STRLEN                                                           STRLEN
    
    
    
    PROTOTYPE:
    
        int strlen(char *string)
    
    
    ARGUMENTS:
    
        string  - Pointer to a character string
    
    
    RETURN VALUE:
    
        The length of the string
    
    
    DECRIPTION:
    
          Returns the length in character of the passed string.  The  length
       does not include the zero byte which terminates the string.
    
    
    EXAMPLES:
    
        length = strlen(command);

    STRLWR                                                           STRLWR
    
    
    
    PROTOTYPE:
    
        strlwr(char *string)
    
    
    ARGUMENTS:
    
        string  - String to convert to lower case
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function converts any  characters  in  the  specified  string
       which were originally in UPPER case to LOWER case. After the function
       has completed, all alphabetic characters in the  string  will  be  in
       LOWER case.
    
    
    EXAMPLES:
    
        strlwr(comand);
        if(!strcmp(command, "quit"))
            exit(0);

    STRNCAT                                                         STRNCAT
    
    
    
    PROTOTYPE:
    
        char *strncat(char *dest, *source, unsigned length)
    
    
    ARGUMENTS:
    
        dest    - Pointer to destination string
        source  - Pointer to source string
        length  - Maximum number of characters to copy
    
    
    RETURN VALUE:
    
        Pointer to zero terminating destination string
    
    
    DESCRIPTION:
    
          This function concatinates the source string onto the tail of  the
       destination string. If the source string exceeds  "length"  bytes  in
       size, only that many characters are copied.
    
    
    EXAMPLES:
    
        strncat(path, filename, 64);

    STRNCMP                                                         STRNCMP
    
    
    
    PROTOTYPE:
    
        int strncmp(char *string1, char *string2, unsigned length)
    
    
    ARGUMENTS:
    
        string1 - Pointer to first string
        string2 - Pointer to second string
        length  - Number of bytes to compare
    
    
    RETURN VALUE:
    
        0   - Strings match exactly
        1   - String1 is greater than string2
        -1  - String2 is greater than string1
    
    
    DESCRIPTION:
    
          This function compares two strings character  by  character  until
       either a difference is detected, or  "length"  characters  have  been
       compared. If the two string portions are identical,  a  zero  (0)  is
       returned. If the first string is greater than the second (as  far  as
       ASCII is concerned), a one (1) is returned. If the second  string  is
       greater, a negative one (-1) is returned.
    
    
    EXAMPLES:
    
        len = strlen(buffer) - 3;
        for(i=1; i < len; ++i)
            if(strncmp(&buffer[i], "***", 3)
                abort("Found three stars\n");

    STRNCPY                                                         STRNCPY
    
    
    
    PROTOTYPE:
    
        strncpy(char *dest, char *source, unsigned length)
    
    
    ARGUMENTS:
    
        dest    - Pointer to destination string
        souce   - Pointer to source string
        length  - Number of bytes to copy
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function copies "length" characters from the source string to
       the  destination  string.  If  the  source  string  is  shorter  than
       "length", the destination string is padded with nulls. If the  source
       string is longer than "length", only that many characters are copied,
       and the destination string is NOT zero terminated.
    
    
    EXAMPLES:
    
        strncpy(filename, argv[1], 64);

    STRNICMP                                                       STRNICMP
    
    
    
    PROTOTYPE:
    
        int strnicmp(char *string1, char *string2, unsigned length)
    
    
    ARGUMENTS:
    
        string1 - Pointer to first string
        string2 - Pointer to second string
        length  - Number of bytes to compare
    
    
    RETURN VALUE:
    
        0   - Strings match exactly
        1   - String1 is greater than string2
        -1  - String2 is greater than string1
    
    
    DESCRIPTION:
    
          This function compares two strings character by character  without
       case sensitivity until either a difference is detected,  or  "length"
       characters have  been  compared.  If  the  two  string  portions  are
       identical (except for case), a zero (0) is  returned.  If  the  first
       string is greater than the second (as far as ASCII is  concerned),  a
       one (1) is returned. If the second string is greater, a negative  one
       (-1) is returned.
    
    
    EXAMPLES:
    
        len = strlen(buffer) - 3;
        for(i=1; i < len; ++i)
            if(strnicmp(&buffer[i], "abc", 3)
                abort("Found 'ABC'\n");

    STRNSET                                                         STRNSET
    
    
    
    PROTOTYPE:
    
        strnset(char *string, char c, unsigned length)
    
    
    ARGUMENTS:
    
        string  - String to set
        c       - character value to use to set string
        length  - maximum number of characters to set
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          Sets the specified maximum number  of  characters  in  the  passed
       string (up till the '\0'  terminator),  to  the  specified  character
       value.
    
    
    EXAMPLES:
    
        static char s[6] = { "abcd" };  /* s == 'a','b','c','d',0,0 */
        strnset(s, '*', 3);             /* s == '*','*','*','d',0,0 */

    STRPBRK                                                         STRPBRK
    
    
    
    PROTOTYPE:
    
        char *strpbrk(char *string, char *set)
    
    
    ARGUMENTS:
    
        string  - String to test
        set     - Set of characters to look for
    
    
    RETURN VALUE:
    
        Pointer to first character from set occuring in string
        Zero (0) if no characters from the set were found
    
    
    DESCRIPTION:
    
          Scans  the  specified  string  for  the  first  occurance  of  any
       character in the given set.
    
    
    EXAMPLES:
    
        if(strpbrk(command, "()[]{}"))
            printf("Brackets of any form are not supported!");

    STRRCHR                                                         STRRCHR
    
    
    
    PROTOTYPE:
    
        char *strrchr(char *string, char chr)
    
    
    ARGUMENTS:
    
        string  - Pointer to a character string
        chr     - Character to look for
    
    
    RETURN VALUE:
    
        Pointer to the last occurance of 'chr' in 'string'
        Zero (0) if character was not found
    
    
    DECRIPTION:
    
          Searches the passed string for the last occurance of the specified
       character. If the character is found, a pointer to  its  position  in
       the string is returned. If the character is not found, a null pointer
       is returned.
    
    
    EXAMPLES:
    
        last_comma = strchr(buffer, ',');

    STRREV                                                           STRREV
    
    
    
    PROTOTYPE:
    
        strrev(char *string)
    
    
    ARGUMENTS:
    
        string  - character string to reverse
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          Reverses the ordering of the characters in the specified string in
       memory.
    
    
    EXAMPLES:
    
        static char s[] = { "ABC" };    /* s == 'A','B','C',0 */
        strrev(s);                      /* s == 'C','B','A',0 */

    STRSET                                                           STRSET
    
    
    
    PROTOTYPE:
    
        strset(char *string, char c)
    
    
    ARGUMENTS:
    
        string  - String to set
        c       - character value to use to set string
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          Sets all characters  in  the  passed  string  (up  till  the  '\0'
       terminator), to the specified character value.
    
    
    EXAMPLES:
    
        static char s[6] = { "abcd" };  /* s == 'a','b','c','d',0,0 */
        strset(s, '*');                 /* s == '*','*','*','*',0,0 */

    STRSPN                                                           STRSPN
    
    
    
    PROTOTYPE:
    
        int strspn(char *string, char *set
    
    
    ARGUMENTS:
    
        string  - String to test
        set     - Set of characters to look for
    
    
    RETURN VALUE:
    
        Length of string segment containing only characters in set.
    
    
    DESCRIPTION:
    
          Scans a string for an "initial segment" containing only characters
       from  the  specified  set.  The  value  returned  is  the  number  of
       characters at the beginning of the specified string  which  occur  in
       the specified set.
    
    
    EXAMPLES:
    
        digit_length = strspn(command, "0123456789");

    STRSTR                                                           STRSTR
    
    
    
    PROTOTYPE:
    
        char *strstr(char *string1, char *string2)
    
    
    ARGUMENTS:
    
        string1 - Pointer to character string to test
        string2 - Pointer to substring to search for
    
    
    RETURN VALUE:
    
        Pointer to substring, or 0 if not found
    
    
    DECRIPTION:
    
          Searches the passed "string1"  for  the  first  occurance  of  the
       passed "string2". If found,  a  pointer  to  the  beginning  of  that
       substring within "string1" is returned.
    
    
    EXAMPLES:
    
        if(ptr = strstr(command, "delete"))
            delete_file(&ptr[6]);

    STRTOK                                                           STRTOK
    
    
    
    PROTOTYPE:
    
        char *strtok(char *string, char *delim)
    
    
    ARGUMENTS:
    
        string  - String to parse (NULL = continue parsing last string)
        delim   - Delimiter characters
    
    
    RETURN VALUE:
    
        Pointer to token parsed from string
        Zero (0) if no more tokens are available
    
    
    DESCRIPTION:
    
          Parses a "token" from the specified string,  using  the  specified
       set of delimiters.
    
          Any delimiter characters  at  the  beginning  of  the  string  are
       skipped, then all non-delimiter characters are preserved, and a  '\0'
       terminator is inserted at the  end  of  the  non-delimiter  character
       string. A pointer to the  first  non-delimiter  character  string  is
       returned.
    
          If called with a NULL (0) pointer to "string", this function  will
       parse the next available token from the previous argument string.
    
       NOTE: The argument "string" is modified by this function.
    
    
    EXAMPLES:
    
        ptr = strtok("this is.a,test", " .,");  /* ptr -> "this" */
        ptr = strtok(NULL, " .,");              /* ptr -> "is"   */
        ptr = strtok(NULL, " .,");              /* ptr -> "a"    */
        ptr = strtok(NULL, " .,");              /* ptr -> "test" */
        ptr = strtok(NULL, " .,");              /* ptr == NULL   */

    STRUPR                                                           STRUPR
    
    
    
    PROTOTYPE:
    
        strupr(char *string)
    
    
    ARGUMENTS:
    
        string  - String to convert to upper case
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function converts any  characters  in  the  specified  string
       which were originally in LOWER case to UPPER case. After the function
       has completed, all alphabetic characters in the  string  will  be  in
       UPPER case.
    
    
    EXAMPLES:
    
        strlwr(comand);
        if(!strcmp(command, "QUIT"))
            exit(0);

    SYSTEM                                                           SYSTEM
    
    
    
    PROTOTYPE:
    
        int system(char *command)
    
    
    ARGUMENTS:
    
        command - A system command to be executed
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          The SYSTEM function accepts any  operating  system  command  as  a
       string parameter, and passes that command to the operating system  to
       be executed.
    
          When the command has terminated,  execution  will  resume  in  the
       MICRO-C program, with the statement following the call to SYSTEM.
    
    
    EXAMPLES:
    
        system("DEL *.TMP");

    TOLOWER                                                         TOLOWER
    
    
    
    PROTOTYPE:
    
        char tolower(char c)
    
    
    ARGUMENTS:
    
        c   - Any character value
    
    
    RETURN VALUE:
    
        The value of 'c', converted to lower case
    
    
    DESCRIPTION:
    
          Returns the value of 'c' converted to lower case. If 'c' is not  a
       letter of upper case, no change is made, and the  original  value  of
       'c' is returned.
    
    
    EXAMPLES:
    
        input_char = tolower(getc(stdin));

    TOUPPER                                                         TOUPPER
    
    
    
    PROTOTYPE:
    
        char toupper(char c)
    
    
    ARGUMENTS:
    
        c   - Any character value
    
    
    RETURN VALUE:
    
        The value of 'c', converted to upper case
    
    
    DESCRIPTION:
    
          Returns the value of 'c' converted to upper case. If 'c' is not  a
       letter of lower case, no change is made, and the  original  value  of
       'c' is returned.
    
    
    EXAMPLES:
    
        putc(toupper(output_char), stdout);

    WRITE                                                             WRITE
    
    
    
    PROTOTYPE:
    
        int write(char *block, int size, HANDLE fh)
    
    
    ARGUMENTS:
    
        block   - Pointer to a block of data to write
        size    - Number of bytes to write
        fh      - File handle of an output file
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          This function writes a block of data to the indicated  file  using
       low level (unbuffered) I/O from memory at the specified address. Data
       is  written  in  "raw"  form,  with  no  translations  of   "newline"
       characters etc. If the value returned is less than the value  of  the
       "size" parameter, some error condition  has  occured  (Such  as  disk
       full).
    
    
    EXAMPLES:
    
        if(write(buffer, 100, fh) < 100)
            abort("File write error\n");

    MICRO-C Library                                                  Page: 3


    
                      +---------------------------------+
                      |                                 |
                      |  *****************************  |
                      |  * The IBM-PC/MS-DOS library *  |
                      |  *****************************  |
                      |                                 |
                      +---------------------------------+
    
    
    
    
    
    
    
    
    
    
       1.2 IBM-PC/MS-DOS Library
    
             The library functions described  on  the  following  pages  are
          available only under the MS-DOS operating  system,  on  IBM-PC  or
          compatible systems.
    
             These routines perform operations which are closely tied to the
          8086 family of processors, the  IBM-PC  hardware,  or  the  MS-DOS
          operating system, and are therefore impractical to implement on  a
          "general" basis.

    ALLOCA                                                           ALLOCA
    
    
    
    PROTOTYPE:
    
        char *alloca(int size)
    
    
    ARGUMENTS:
    
        size    - Size of memory block to allocate (in bytes).
    
    
    RETURN VALUE:
    
        0       - Memory allocation failed
        !0      - Pointer to allocated memory
    
    
    DESCRIPTION:
    
          The "alloca" function  allocates  a  block  of  automatic  (stack)
       memory, which exists only only until the  function  calling  "alloca"
       returns. When that function returns, all stack memory  including  any
       allocated by "alloca" is released.
    
       NOTE: THE FOLLOWING RESTRICTIONS APPLY TO THE USE OF ALLOCA:
    
          The function calling 'alloca' MUST have  at  least  one  automatic
       (local) variable, otherwise MICRO-C will not  restore  the  stack  on
       exit.
    
          The 'alloca' function must be used within a simple expression,  at
       a point where there will be no partial results stored on the stack.
    
          The above conditions can best be met by declaring a local  pointer
       which will hold the memory address, and assigning it the value of the
       'alloca' call in a single statement. The address returned by 'alloca'
       should NOT be assigned to a calculated  address  (such  as  an  array
       element or indirect reference via a pointer), since this  may  result
       in stack activity.
    
          NOTE: The size operand to 'alloca' can be  a  complex  expression,
       since any stack operations it causes will have dissipated by the time
       'alloca' gets called.
    
    
    EXAMPLES:
    
    func(string)
        char *string;
    {
        char *local_memory;
    
        if(!(local_memory = alloca(strlen(string)+1)))
            abort("Not enough memory for alloca");
        /* ... */
    }

    ALLOC_SEG                                                     ALLOC_SEG
    
    
    
    PROTOTYPE:
    
        int alloc_seg(int size)
    
    
    ARGUMENTS:
    
        size    - Number of 16 byte paragraphs to allocate
    
    
    RETURN VALUE:
    
    
        0       - Not enough free memory available
        !0      - The segment address of the allocated memory
    
    
    DESCRIPTION:
    
          The "alloc_seg" function allocates a 'segment' of memory from DOS.
       The size is given in 16 byte "paragraphs". The allocated memory  will
       be outside of the data memory available to the MICRO-C  program,  and
       therefore must be accessed via assembly lenguage functions,  or  with
       the "peek" and "poke" library functions.
    
    
    EXAMPLES:
    
        if(!(aseg = alloc(4096)))   /* Get a 64K data segment */
            abort("Not enough memory!!!");
        set_es(aseg);               /* Set up extra segment */
        asm_func();                 /* Invoke assembler function */

    BEEP                                                               BEEP
    
    
    
    PROTOTYPE:
    
        beep(unsigned freq, unsigned length)
    
    
    ARGUMENTS:
    
        freq    - frequency (in hertz) of tone to generate
        length  - Length (in milliseconds) of tone
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function generates a tone of the specified frequency, for the
       specified duration. It is useful for giving an audible signal.
    
    
    EXAMPLES:
    
        beep(1000, 1000);   /* 1000Hz tone for 1000ms (1 second) */

    BREAK                                                             BREAK
    
    
    
    PROTOTYPE:
    
        break(int allow)
    
    
    ARGUMENTS:
    
        allow   - 0 = disallow break, !0 = allow breaks
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          Controls the setting of the DOS "break" flag. When set  on  (allow
       != 0), the keyboard is tested for CONTROL-BREAK on any  DOS  function
       call. If set off (allow == 0), CONTROL-C is  only  recognized  during
       I/O to the keyboard and video display.
    
    
    EXAMPLES:
    
        break(1);   /* Disable keyboard interrupts */

    CCLOSE                                                           CCLOSE
    
    
    
    PROTOTYPE:
    
        Cclose()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function closes the  communications  port  previously  opened
       using "Copen". The system interrupt vectors and all  other  hooks  to
       the comm port are restored.
    
          This function must be called  before  any  program  using  "Copen"
       terminates, otherwise the communications port  will  be  left  in  an
       indeterminate state. If this is not done, there will be a possibility
       of system crash if an interrupt is received from the port  after  the
       program has terminated.
    
    
    EXAMPLES:
    
        Cclose();       /* Close comm port */
        exit(0);        /* And terminate */

    CGETC                                                             CGETC
    
    
    
    PROTOTYPE:
    
        int Cgetc()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        Character read from the communications port
    
    
    DESCRIPTION:
    
          This function reads a single  character  from  the  communications
       port previously opened with "Copen". If no  character  is  available,
       "Cgetc" will wait for one.
    
    
    EXAMPLES:
    
        /* Get a string from the comm port */
        while((c = cgetc()) != '\r')
            *ptr++ = c;
        *ptr = 0;

    COPEN                                                             COPEN
    
    
    
    PROTOTYPE:
    
        int Copen(int port, int speed, int mode, int modem)
    
    
    ARGUMENTS:
    
        port    - Comm port to use (1, 2, 3 or 4)
        speed   - Baudrate divisor to set
        mode    - Communications parameters to set
        modem   - Modem control lines to set
    
    RETURN VALUE:
    
        0       - Successful open
        !0      - Requested comm port is not available
    
    
    DESCRIPTION:
    
          The "Copen" function opens a serial communications port on the IBM
       PC for access. An independant interrupt handler and I/O  drivers  are
       installed, which allow high speed full duplex operation of the serial
       port with optional XON/XOFF flow control of both receive and transmit
       streams.
    
          Only one serial port  may  be  accessed  at  a  time  using  these
       functions, If "Copen" is called more than once, it will automatically
       close the last port before opening the new one.
    
          The meaning of the "speed",  "mode",  and  "modem"  parameters  if
       documented in the "comm.h" header file.
    
          An external "char" variable "Cflags" may be accessed to enable  or
       disable transparency of the serial  channel.  When  "transparent"  is
       selected, XON/XOFF flow control is disabled, and all data is sent and
       received with no changes. When  operating  in  this  mode,  you  must
       insure that "Cgetc" is called frequently enough  that  the  256  byte
       internal receive buffer will not overflow.
    
          Since "Cflags" is  used  by  the  interrupt  handler,  you  should
       disable and enable interrupts around any accesses to it.

    
    
    
    EXAMPLES:
    
        #include comm.h     /* Get comm port defintions */
    
            extern char Cflags;
    
        /*
         * Program to read & echo characters on the serial port
         * in transparent mode. (Until ESCAPE char is received)
         */
        main()
        {
            char c;
    
            if(Copen(1, _2400, PAR_NO|DATA_8|STOP_1, SET_RTS|SET_DTR))
                abort("Cannot access COM1");
    
            disable();                  /* Disable interrupts */
            Cflags |= TRANSPARENT;      /* Set transparency */
            enable();                   /* Re-enable interrupts */
    
            while((c = Cgetc()) != 0x1B)    /* Do until ESCAPE */
                Cputc(c);
    
            Cclose();                   /* Close the serial port */
        }

    COPY_SEG                                                       COPY_SEG
    
    
    
    PROTOTYPE:
    
        copy_seg(int dseg, int doffset, int sseg, int soffset, int size)
    
    
    ARGUMENTS:
    
        dseg    - Destination segment
        doffset - Destination offset
        sseg    - Source segment
        soffset - Source offset
        size    - Number of bytes to copy
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function  perform  a  copy  between  80X86  processor  memory
       segments. A number of bytes equal to "size" is copied from the source
       segment and offset to the destination segment and offset.
    
    
    EXAMPLES:
    
        /* Save the video display contents */
        copy_seg(get_ds(), buffer, _V_BASE, 0, (25*80)*2);

    CPU                                                                 CPU
    
    
    
    PROTOTYPE:
    
        int cpu()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        0       - CPU is 8088 or 8086
        1       - CPU is 80188 or 80186
        2       - CPU is 80286
        3       - CPU is 80386 or 80486
    
    
    DESCRIPTION:
    
          This function  returns  a  simple  integer  which  identifies  the
       processor type on which the program is currently executing.
    
    
    EXAMPLES:
    
        if(cpu() < 2)
            abort("This program requires at least an 80286");

    CPUTC                                                             CPUTC
    
    
    
    PROTOTYPE:
    
        Cputc(char c)
    
    
    ARGUMENTS:
    
        c       - Character to write to communciation port
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The  "Cputc"  function  writes  the   given   character   to   the
       communcinations port previously opened by "Copen".
    
    
    EXAMPLES:
    
        while(*ptr)         /* Write a string to comm port */
            Cputc(*ptr++);

    CSIGNALS                                                       CSIGNALS
    
    
    
    PROTOTYPE:
    
        int Csignals()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        The modem input signals read from the open comm port
    
    
    DESCRIPTION:
    
          This function reads the modem input signals (DSR, CD, RI etc) from
       the serial communication  port  previously  opened  by  "Copen",  and
       returns them as an integer value.
    
          The meaning of the  individual  bits  in  the  value  returned  by
       "Csignals" is documented in the "comm.h" header file.
    
    
    EXAMPLES:
    
        if(!(Csignals() & DSR)) {
            Cclose();
            abort("Modem not ready"); }

    CTESTC                                                           CTESTC
    
    
    
    PROTOTYPE:
    
        int Ctestc()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        0-255   - Character read from comm port
        -1      - No character available
    
    
    DESCRIPTION:
    
          This function tests for a character from the  communications  port
       previously opened with "Copen", and returns that character if one  if
       found. If no character is available, "Ctestc" returns -1.
    
    
    EXAMPLES:
    
        if((c = Ctestc()) == -1) {
            Cclose();
            abort("No character available"); }

    DELAY                                                             DELAY
    
    
    
    PROTOTYPE:
    
        delay(int msec)
    
    
    ARGUMENTS:
    
        msec    - Number of milliseconds to wait
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          Pauses for the specified number of milliseconds. This function  is
       limited to the accuracy of the BIOS clock,  which  operates  at  18.2
       ticks per second.
    
    
    EXAMPLES:
    
        delay(1000);        /* Wait one second */

    DISABLE                                                         DISABLE
    
    
    
    PROTOTYPE:
    
        disable()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The  "disable"  function  disables  the  8086  interrupt   system,
       preventing the  processor  from  servicing  interrupts.  It  is  used
       whenever the execution of an interrupt handler may interfere  with  a
       particular operation.
    
          When this function is used, the "enable" function should be called
       as soon as possible after "disable". Failure to do this may result in
       loss  of  system  functions  performed  under  interrupts,  such   as
       timekeeping, and serial communications (Via MICRO-C serial drivers).
    
    
    EXAMPLES:
    
        disable();                  /* Disallow interrupts */
        Cflags &= ~TRANSPARENT;     /* Remove transparency */
        enable();                   /* Re-allow interrupts */

    ENABLE                                                           ENABLE
    
    
    
    PROTOTYPE:
    
        enable()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "enable" function enables the 8086 interrupt system,  allowing
       the processor to service interrupts. It should be called as  soon  as
       possible following the use of the "disable" function.
    
    
    EXAMPLES:
    
        disable();                  /* Disallow interrupts */
        Cflags |= TRANSPARENT;      /* Force  transparency */
        enable();                   /* Re-allow interrupts */

    EXEC                                                               EXEC
    
    
    
    PROTOTYPE:
    
        int exec(char *exefile, char *args)
    
    
    ARGUMENTS:
    
        exefile - Full pathname of a '.COM' or '.EXE' file
        args    - Command tail containing arguments
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an MS-DOS error code
    
    
    DESCRIPTION:
    
          The "exec" function causes MS-DOS to suspend the execution of  the
       MICRO-C program, and then to execute the indicated '.EXE'  or  '.COM'
       program file. When that program terminates, execution of the  MICRO-C
       program will resume.
    
          This is a low level interface to the MS-DOS 'EXEC'  function,  and
       as such, it does not search your PATH, does not process '.BAT' files,
       nor provide any I/O redirection facilities. If you want to  make  use
       of these features (which are  provided  by  'COMMAND.COM'),  use  the
       higher level 'SYSTEM' function.
    
    
    EXAMPLES:
    
        printf("Type 'EXIT' to return to the MICRO-C program\n");
        exec("C:\\COMMAND.COM", "");    /* Start up a sub-shell */

    FREE_SEG                                                       FREE_SEG
    
    
    
    PROTOTYPE:
    
        int free_seg(int segment)
    
    
    ARGUMENTS:
    
        segment - A previously allocated segment of memory
    
    
    RETURN VALUE:
    
        0       - The segment was released
        !0      - DOS error code
    
    
    DESCRIPTION:
    
          The "free_seg" function releases a segment  of  memory  previously
       allocated by "alloc_seg", and returns it  to  the  operating  system.
       This should be used whenever your program has finished with a segment
       of extra memory which it has allocated.
    
    
    EXAMPLES:
    
        aseg = alloc_seg(4096);         /* Allocate a 64K segment */
        set_es(aseg);                   /* Set up extra segment */
        asm_func();                     /* Call assembler function */
        free_seg(aseg);                 /* Releas the memory */

    GET_ATTR                                                       GET_ATTR
    
    
    
    PROTOTYPE:
    
        int get_attr(char *pathname, int &attrs)
    
    
    ARGUMENTS:
    
        pathname- Name of file to get attributes of
        attrs   - Integer to receive attributes
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          This function retreives the attributes of the specified file.
    
          The meaning of the individual bits in the "attrs" value is defined
       in the "file.h" header file.
    
    
    EXAMPLES:
    
        get_attr("tempfile", &attributes);

    GET_CS                                                           GET_CS
    
    
    
    PROTOTYPE:
    
        int get_cs()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        The current processor CODE segment
    
    
    DESCRIPTION:
    
          This function is available only on the 8086 family of  processors,
       and returns the current processor CODE segment.
    
    
    EXAMPLES:
    
        code_seg = get_cs();

    GET_DATE                                                       GET_DATE
    
    
    
    PROTOTYPE:
    
        get_date(int &day, int &month, int &year)
    
    
    ARGUMENTS:
    
        &day    - Address of integer to receive day (1-31)
        &month  - Address of integer to receive month (1-12)
        &year   - Address of integer to receive year (1980-2099)
    
    
    RETURN VALUE:
    
        Day of week (0=Sun ... 6=Sat)
    
    
    DESCRIPTION:
    
          This function gets the current system  date  in  day,  month,  and
       year.
    
    
    EXAMPLES:
    
        get_date(&day, &month, &year);
        printf("%s %u, %u", months[month], day, year);

    GET_DRIVE                                                     GET_DRIVE
    
    
    
    PROTOTYPE:
    
        int get_drive()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        The currently active (default) disk drive (0=A, 1=B, 2=C, ...)
    
    
    DESCRIPTION:
    
          The "get_drive" function returns the  drive  index  (0-n)  of  the
       currently active or "default" MS-DOS disk drive.
    
    
    EXAMPLES:
    
        old_drive = get_drive();
        set_drive(new_drive);

    GET_DS                                                           GET_DS
    
    
    
    PROTOTYPE:
    
        int get_ds()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        The current processor DATA segment
    
    
    DESCRIPTION:
    
          This function is available only on the 8086 family of  processors,
       and returns the current processor DATA segment.
    
    
    EXAMPLES:
    
        data_seg = get_ds();

    GET_ES                                                           GET_ES
    
    
    
    PROTOTYPE:
    
        int get_es()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        The current processor EXTRA segment
    
    
    DESCRIPTION:
    
          This function is available only on the 8086 family of  processors,
       and returns the current processor EXTRA segment.
    
    
    EXAMPLES:
    
        code_seg = get_es();

    GET_TIME                                                       GET_TIME
    
    
    
    PROTOTYPE:
    
        get_time(int &hour, int &minite, int &second)
    
    
    ARGUMENTS:
    
        &hour   - Address of integer to receive hour (0-23)
        &minite - Address of integer to receive minite (0-59)
        &second - Address of integer to receive second (0-59)
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function gets the current system time in hours,  minites  and
       seconds.
    
    
    EXAMPLES:
    
        get_time(&hour, &minite, &second);
        printf("%02:%02:%02", hour, minite, second);

    INT86                                                             INT86
    
    
    
    PROTOTYPE:
    
        int int86(int inum)
    
    
    ARGUMENTS:
    
        inum    - The 8086 software interrupt to execute
    
    
    RETURN VALUE:
    
        8086 FLAGS register after interrupt executes.
    
    
    DESCRIPTION:
    
          This  function  performs  an  8086  software   interrupt.   Before
       executing the interrupt, the processor registers are loaded from  the
       external "int" variables: _AX_, _BX_, _CX_, _DX_, _SI_ and _DI_.  The
       DS, ES and SS segment registers are all set  to  point  to  MICRO-C's
       data segment.
    
          After the interrupt  completes,  the  contents  of  the  processor
       registers are copied to the above named variables.
    
    
    EXAMPLES:
    
        extern int _AX_, _DX_;
        main() {
            _AX_ = 0x0200;  /* MSDOS function 2 - Output character */
            _DX_ = '$';     /* Character to output */
            int86(0x21);    /* Call MSDOS */
        }

    RESIZE_SEG                                                   RESIZE_SEG
    
    
    
    PROTOTYPE:
    
        int resize_seg(int segment, int size)
    
    
    ARGUMENTS:
    
        segment - A previously allocated segment of memory
        size    - Desired size (in 16 byte paragraphs)
    
    
    RETURN VALUE:
    
        0       - The segments size has been adjusted
        !0      - DOS error code
    
    
    DESCRIPTION:
    
          The "resize_seg" function provides a method of changing  the  size
       of a segment of memory previously allocated via "alloc_seg".  If  not
       enough memory is available, the function will fail  with  a  ono-zero
       return value.
    
          This function may also be used to adjust the memoey allocation  of
       the programs image, by passing it the segment address of the programs
       own PSP. This value is available in the external variable "PSP".
    
          MICRO-C normally allocates 64K for programs compiled in  the  TINY
       model, and (64K + (256 byte PSP) + (size  of  executable  code))  for
       programs compiled in the SMALL model. This allocation should NEVER be
       reduced, however you may enlarge it if your program wishes to  access
       additional data immediately following its own DATA/STACK segment.
    
    
    EXAMPLES:
    
        extern int PSP;
    
        main()
        {
            if(resize_seg(PSP, 8192))   /* Append 64K buffer */
                abort("Not enough memory!!!");
            ...     /* Remainder of program */
        }

    RESTORE_VIDEO                                             RESTORE_VIDEO
    
    
    
    PROTOTYPE:
    
        restore_video(char buffer[4006]);
    
    
    ARGUMENTS:
    
        buffer  - Video save area.
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The RESTORE_VIDEO function restores the contents and state of  the
       IBM P.C. video display to the state it was in when  "SAVE_VIDEO"  was
       executed. At the present time, the function  is  effective  only  for
       text modes. Graphics screens will not be restored, due  to  the  high
       memory requirements.
    
          Although this function is useful in ANY program  (to  restore  the
       DOS screen before termination), it is most  useful  in  "POP-UP"  ram
       resident programs (See "TSR" function), to save  the  screen  of  any
       application which may be running when you pop up.
    
          The video state is restored from  the  passed  "buffer"  argument,
       which is 4006 bytes  in  size,  and  must  have  been  filled  in  by
       "SAVE_VIDEO". It has the following format:
    
                  buffer[0]         - Video mode
                    "   [1]         - Video page
                    "   [2]         - 'X' cursor position
                    "   [3]         - 'Y' cursor position
                    "   [4]         - Ending line for cursor
                    "   [5]         - Starting line for cursor
                    "   [6-4005]    - Saved video screen contents
    
    
    EXAMPLES:
    
        popup_func()
        {
            save_video();
            perform_function();
            restore_video();
        }

    SAVE_VIDEO                                                   SAVE_VIDEO
    
    
    
    PROTOTYPE:
    
        save_video(char buffer[4006]);
    
    
    ARGUMENTS:
    
        buffer  - Video save area.
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The SAVE_VIDEO function saves the current contents  and  state  of
       the IBM P.C. video display. The screen may be restored  at  any  time
       using "RESTORE_VIDEO". At the present time, the function is effective
       only for text modes. Graphics screens will not be saved, due  to  the
       high memory requirements.
    
          Although this function is useful in ANY program  (to  restore  the
       DOS screen before termination), it is most  useful  in  "POP-UP"  ram
       resident programs (See "TSR" function), to save  the  screen  of  any
       application which may be running when you pop up.
    
          The video state is saved in the passed "buffer" argument, which is
       4006 bytes in size, and has the following format:
    
                  buffer[0]         - Video mode
                    "   [1]         - Video page
                    "   [2]         - 'X' cursor position
                    "   [3]         - 'Y' cursor position
                    "   [4]         - Ending line for cursor
                    "   [5]         - Starting line for cursor
                    "   [6-4005]    - Saved video screen contents
    
    
    EXAMPLES:
    
        popup_func()
        {
            save_video();
            perform_function();
            restore_video();
        }

    SET_ATTR                                                       SET_ATTR
    
    
    
    PROTOTYPE:
    
        int set_attr(char *pathname, int attrs)
    
    
    ARGUMENTS:
    
        pathname- Name of file to get attributes of
        attrs   - New attributes
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          This function sets the system attributes of the specified file.
    
          The meaning of the individual bits in the "attrs" value is defined
       in the "file.h" header file.
    
    
    EXAMPLES:
    
        set_attr("tempfile", READONLY|HIDDEN);

    SET_DATE                                                       SET_DATE
    
    
    
    PROTOTYPE:
    
        set_date(int day, int month, int year)
    
    
    ARGUMENTS:
    
        day     - New day (1-31)
        month   - New month (1-12)
        year    - New year (1980-2099)
    
    
    RETURN VALUE:
    
        0       - Success
        -1      - Invalid date given
    
    
    DESCRIPTION:
    
          This function sets the current system  date  to  day,  month,  and
       year.
    
    
    EXAMPLES:
    
        set_date(1, 1, 1980);   /* Set to Jan 1, 1980 */

    SET_DRIVE                                                     SET_DRIVE
    
    
    
    PROTOTYPE:
    
        int set_drive(int drive)
    
    
    ARGUMENTS:
    
        Drive   - New drive index (0=A, 1=B, 2=C ...)
    
    
    RETURN VALUE:
    
        The total number of "logical" disk drives in the system
    
    
    DESCRIPTION:
    
          The "set_drive" function sets the  disk  drive  indicated  by  the
       "drive" index (0-x) to be the currently active  or  "default"  MS-DOS
       disk drive.
    
    
    EXAMPLES:
    
        old_drive = get_drive();
        set_drive(new_drive);

    SET_ES                                                           SET_ES
    
    
    
    PROTOTYPE:
    
        int set_es(int segment)
    
    
    ARGUMENTS:
    
        segment - The 16 bit new segment value
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function is available only on the 8086 family of  processors,
       and sets the processors EXTRA segment to the indicated value.
    
    
    EXAMPLES:
    
        set_es(get_ds());       /* Copy DATA to EXTRA segments */

    SET_TIME                                                       SET_TIME
    
    
    
    PROTOTYPE:
    
        set_time(int hour, int minite, int second)
    
    
    ARGUMENTS:
    
        hour    - New hour (0-23)
        minite  - New minite (0-59)
        second  - New second (0-59)
    
    
    RETURN VALUE:
    
        0       - Success
        -1      - Invalid time given
    
    
    DESCRIPTION:
    
          This function sets the current system time to "hour", "minite" and
       "second".
    
    
    EXAMPLES:
    
        set_time(0, 0, 0);  /* Set to 00:00:00 (midnight) */

    SOUND                                                             SOUND
    
    
    
    PROTOTYPE:
    
        sound(unsigned freq)
    
    
    ARGUMENTS:
    
        freq    - frequency (in hertz) of tone to generate
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          Turns on the IBM PC speaker to generate a tone  at  the  specified
       frequency. The tone will continue to be generated until either a  new
       tone is output, or a call to sound_off() is performed.
    
    
    EXAMPLES:
    
        sound(1000);    /* Generate a 1000hz tone */
        delay(1000);    /* For 1000 ms (1 second) */
        sound_off();    /* Terminate the tone */

    SOUND_OFF                                                     SOUND_OFF
    
    
    
    PROTOTYPE:
    
        sound_off()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function terminates a tone previously  established  with  the
       sound() function. The PC speaker is silenced.
    
    
    EXAMPLES:
    
        sound(1000);    /* Generate a 1000hz tone */
        delay(1000);    /* For 1000 ms (1 second) */
        sound_off();    /* Terminate the tone */

    TSR                                                                 TSR
    
    
    
    PROTOTYPE:
    
        tsr(&func, int hotkey, int alloc)
    
    
    ARGUMENTS:
    
        func    - Address of function to execute
        hotkey  - POP-UP activation hotkeys
        alloc   - Memory allocation
    
    
    RETURN VALUE:
    
        Function normally never returns, but if it does, an
        operating system error code is passed back.
    
    
    DESCRIPTION:
    
          The TSR function terminates the MICRO-C  program,  but  leaves  it
       resident in memory. When the specified "HOT KEYS" are detected on the
       IBM PC keyboard, the context of whatever program is running is saved,
       and the specified MICRO-C function  is  called.  When  that  function
       returns, the interrupted program is resumed.
    
          When activated this way, THE "func" FUNCTION  MUST  NOT  TERMINATE
       WITH "exit" or one of its related functions (abort  etc.).  THE  ONLY
       WAY IT MAY TERMINATE IS TO "return" NORMALLY.
    
          The meaning of "hotkey" is defined in the "tsr.h" header file.
    
          The "alloc" paremeter specifies how much extra  memory  is  to  be
       retained in the TSR image for use  by  the  MICRO-C  stack  and  heap
       memory allocation functions. The "func" function(s) must insure  that
       the total amount of memory used by the stack and  calls  to  "malloc"
       does not exceed this value.
    
          NOTE: "malloc" will fail if the heap grows to  within  1K  of  the
       stack pointer.
    
          All memory used by  code,  global  variables,  string  space,  and
       "malloc" calls prior to the use of "tsr" is  automatically  retained,
       and should not be included in the "alloc" value.
    
          TSR programs which perform screen I/O should take care to save and
       restore the screen contents when popping up and down.
    
    
    EXAMPLES:
    
        tsr(&popup_func, ALT+L_SHIFT, 1024);

    VCLEAR_BOX                                                   VCLEAR_BOX
    
    
    
    PROTOTYPE:
    
        vclear_box(int x, int y, int w, int h)
    
    
    ARGUMENTS:
    
        x       - COLUMN of top left corner of box
        y       - ROW of top left corner of box
        w       - Width of box (columns)
        h       - Height of box (rows)
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function clears a box of the specified height and  width,  at
       the indicated 'X' and 'Y' coordinates, on  the  IBM-PC  video  screen
       using the block graphics characters. The entire  box  is  cleared  to
       spaces.
    
          "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        vclear_box(21, 11, 8, 3);   /* Clear a BOX */

    VCLEOL                                                           VCLEOL
    
    
    
    PROTOTYPE:
    
        vcleol()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function clears the IBM PC  video  screen  from  the  current
       cursor position to the end of a line.
    
          You must "#include video.h", and execute "VOPEN"  prior  to  using
       this function.
    
    
    EXAMPLES:
    
        vprintf("Input> ");     /* Display a prompt */
        vcleol();               /* Clear remainder of input line */

    VCLEOS                                                           VCLEOS
    
    
    
    PROTOTYPE:
    
        vcleos()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function clears the IBM PC  video  screen  from  the  current
       cursor position to the end of a screen.
    
          "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        vgotoxy(0, 10);         /* position at line 11 */
        vcleos();               /* Clear lower part of screen */

    VCLSCR                                                           VCLSCR
    
    
    
    PROTOTYPE:
    
        vclscr()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function clears the entire IBM PC video screen and resets the
       cursor position to the top left hand corner.
    
          "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        if(c = 0x1b) {          /* Escape command */
            vclscr();       /* Clear the screen */
            vprintf("%s has terminated\n", argv[0]);
            exit(-1); }

    VCURSOR_BLOCK                                             VCURSOR_BLOCK
    
    
    
    PROTOTYPE:
    
        vcursor_block()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function enables (turns on) display of the cursor on the  IBM
       PC video display. The cursor is shown as  flashing  block,  occupying
       the entire character window.
    
          "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        if(insert)              /* Test insert mode flag */
            vcursor_block();    /* Indicate inserting with block cursor */
        else
            vcursor_line();     /* Indicate overwrite with line cursor */

    VCURSOR_LINE                                               VCURSOR_LINE
    
    
    
    PROTOTYPE:
    
        vcursor_line()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function enables (turns on) display of the cursor on the  IBM
       PC video display. The cursor is shown as a single flashing  line,  at
       the bottom of the character window.
    
          "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        vcursor_line();     /* Re-enable the cursor */
        exit(0);            /* And terminate */

    VCURSOR_OFF                                                 VCURSOR_OFF
    
    
    
    PROTOTYPE:
    
        vcursor_off()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function inhibits (turns off) display of the  cursor  on  the
       IBM PC video display. This affects the cursor  display  only,  screen
       output will continue to be displayed at the correct cursor position.
    
          "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        vclscr();           /* Clear screen */
        vcursor_off();      /* Inhibit cursor */
        vmenu(10, 10, main_menu, 0, &index);    /* Present main menu */

    VDRAW_BOX                                                     VDRAW_BOX
    
    
    
    PROTOTYPE:
    
        vdraw_box(int x, int y, int w, int h)
    
    
    ARGUMENTS:
    
        x       - COLUMN of top left corner of box
        y       - ROW of top left corner of box
        w       - Width of box (columns)
        h       - Height of box (rows)
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function draws a box of the specified height  and  width,  at
       the indicated 'X' and 'Y' coordinates, on  the  IBM-PC  video  screen
       using the block graphics characters.
    
          "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        vdraw_box(20, 10, 10, 5);   /* Draw a BOX */

    VERSION                                                         VERSION
    
    
    
    PROTOTYPE:
    
        int version()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        MS-DOS operating system version number
    
    
    DESCRIPTION:
    
          The "version" function is available only under MS-DOS, and returns
       the version number of the operating system.
    
          The higher 8 bits  of  the  returned  value  indicates  the  MAJOR
       version number ('3' in DOS 3.1)
    
          The lower 8 bits of the returned value indicates the MINOR version
       nuber ('1' in DOS 3.1).
    
    
    EXAMPLES:
    
        if(version() < 0x031E)
            abort("Requires DOS 3.30 or higher\n");

    VGETC                                                             VGETC
    
    
    
    PROTOTYPE:
    
        int vgetc()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        0-127   - ASCII value of key pressed
        < 0     - Special function key as defined in "video.h"
    
    
    DESCRIPTION:
    
          The "vgetc" function waits until a key is pressed  on  the  system
       console, and returns its value.
    
          Note that due to the  buffering  of  the  IBM-PC  keyboard,  every
       keypress will be reported, even if the VGETC function is called after
       a key is pressed and released.
    
    
    EXAMPLES:
    
        switch(vgetc()) {       /* Handle input keys
                . . .
        }

    VGETS                                                             VGETS
    
    
    
    PROTOTYPE:
    
        int vgets(int x, int y, char *prompt, char *field, int width)
    
    
    ARGUMENTS:
    
        x       - COLUMN of top left corner of input box
        y       - ROW of top left corner of input box
        prompt  - String to prompt with
        field   - String to receive the data
        width   - Width in characters of input field
    
    
    RETURN VALUE:
    
        0   - Selection was made and ENTER pressed.
        !0  - Input was aborted via ESCAPE key.
    
    
    DESCRIPTION:
    
          The "vgets" function draws a  box  on  the  video  screen  at  the
       specified X and Y coordinates, then prompts for and receives an input
       string in the box. The box is  drawn  large  enough  to  contain  the
       prompt and  the  specified  width  of  input  field.  The  prompt  is
       displayed at the left hand  side  of  the  box,  and  the  cursor  is
       positioned immediatly following it, at the start of the input field.
    
          The "field" parameter is the  address  of  a  character  array  to
       receive the input string. The previous value of the "field" array  is
       inserted into the input box when VGETS is invoked. If you do not want
       to display an old value, you should set the first  character  pointed
       to by field to zero, before calling VGETS.
    
          When entering the string, the user may use the  following  special
       keys to edit the input field:
    
                Right Arrow - Move forward one character
                Left  Arrow - Move backward one character
                Delete      - Delete the character under the cursor
                Backspace   - Move backward one character and delete.
                Home        - Move to beginning of string
                End         - Move to end of string
                PgUp        - Clear (erase) entire string
                PgDn        - Clear from cursor to end of string
                Enter       - Accept (enter) the string
                ESC         - Abort the input request
    
          All data entered in the input box is inserted into any data  which
       is already present.

    
    
    
    EXAMPLES:
    
        name[0] = 0;
        if(vgets(10, 10, "Your name?", name, 30))
            return;     /* Aborted, exit to higher level */

    VGOTOXY                                                         VGOTOXY
    
    
    
    PROTOTYPE:
    
        vgotoxy(int x, int y)
    
    
    ARGUMENTS:
    
        x       - New COLUMN (0-79)
        y       - New ROW    (0-24)
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "vgotoxy" function positions the cursor on  the  IBM-PC  video
       screen. Any further display output will occur  at  the  new  ROW  and
       COLUMN on the screen.
    
          The extern "int" variable "V_XY" may be referenced to read or  set
       the  current  X/Y  position.  The  higher  8  bits  contain  the  'Y'
       coordinate, and the lower 8 bits contain the 'X' coordinate. If  this
       variable is used to set (restore) the  cursor  position,  "vupdatexy"
       must then be called to position the physical cursor.
    
          "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        for(i=0; i<24; ++i) {   /* Draw a diagonal line of 'X's */
            vgotoxy(i, i);
            vputc('X'); }

    VMENU                                                             VMENU
    
    
    
    PROTOTYPE:
    
        vmenu(int x, int y, char *names[], char erase, int &index)
    
    
    ARGUMENTS:
    
        x       - COLUMN of top left corner of menu box
        y       - ROW of top left corner of menu box
        names   - Array to menu selection text (last entry = 0)
        erase   - 1=Erase BOX after selection is made
        index   - Address of message selection index variable
    
    
    RETURN VALUE:
    
        0   - Selection was made and ENTER pressed.
        !0  - Menu was aborted via ESCAPE key.
    
    
    DESCRIPTION:
    
          The "vmenu" function displays a list of menu items enclosed  in  a
       box on the IBM-PC video  screen  at  the  specified  ROW  and  COLUMN
       address. The user may use the UP, DOWN, HOME and END keys  to  select
       an entry by moving the INVERSE VIDEO selection cursor.
    
          When the desired selection is under the cursor, the  selection  is
       made by pressing the ENTER key.
    
          At any time the menu selection may be  canceled  by  pressing  the
       ESCAPE key.
    
          The "names" argument must be a pointer to an  array  of  character
       strings which are the selections to display. This array MUST end with
       a zero (0) element to indicate the end of the list.
    
          The "erase" flag indicates that the menu box should be cleared  to
       blanks when the selection is made. If "erase=0", the menu box is left
       on the screen, WITHOUT the selection cursor, with the selected  entry
       marked by '>' and '<'. The menu box is always erased when the menu is
       aborted with the ESCAPE key.
    
          The "index" argument is the address of  an  "int"  variable  which
       contains the position of the selection cursor. It controls where  the
       selection cursor will appear when the function is first invoked (0  =
       first entry), and also is assigned  the  position  of  the  selection
       cursor when the selection is made.

    
    
    
    EXAMPLES:
    
        char *names[] = { "One", "Two", "Three", "Four", "Five", 0 };
            . . .
        index = 0;
        if(vmenu(10, 10, names, 0, &index))
            return;         /* Aborted, exit to higher level */
        switch(index) {     /* Handle selection */
            . . .
        }

    VMESSAGE                                                       VMESSAGE
    
    
    
    PROTOTYPE:
    
        vmessage(int x, int y, char *string)
    
    
    ARGUMENTS:
    
        x       - COLUMN of top left corner of message box
        y       - ROW of top left corner of message box
        string  - Message to display
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "vmessage" function displays a text  string  surrounded  by  a
       BOX, on the IBM-PC video screen, at  the  specified  ROW  and  COLUMN
       address.
    
          "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        vmessage(20, 20, "Press any KEY to continue");
        get_key();
        vclear_box(20, 20, 26, 2);

    VOPEN                                                             VOPEN
    
    
    
    PROTOTYPE:
    
        vopen()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function initializes the IBM-PC video display adapter for use
       with the MICRO-C video library functions. It determines  the  adapter
       type  (COLOR  ot  MONOCHROME),  sets  up  internal   variables   with
       information required by the other video  functions,  and  clears  the
       video screen.
    
          This function MUST  be  called  before  any  of  the  other  video
       functions in the library are used.
    
          After "vopen" is called, the extern "int" variable "V_BASE" may be
       referenced to determine the memory segment of the video display (B000
       for monochrome, B800 for color).
    
          Any program using the video library  functions  must  include  the
       "video.h" header file.
    
    
    EXAMPLES:
    
        vopen();

    VPRINTF                                                         VPRINTF
    
    
    
    PROTOTYPE:
    
        register vprintf(char *format, arg, ...)
    
    
    ARGUMENTS:
    
        format  - Pointer to format string
        arg     - Argument as determined by format string
        ...     - Additional arguments may be required
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function performs exactly as the  "PRINTF"  function  in  the
       standard function library, except that it  outputs  directly  to  the
       video screen using the video interface library routines.
    
          This function should be used in preference to "PRINTF" when  using
       the video function library since "PRINTF" will  not  move  the  video
       librarys cursor.
    
          NOTE: This function uses a variable number of arguments, and  must
       be declared as "register" (See "video.h").
    
          "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        vgotoxy(0, 0);
        vprintf("Screen %u", screen);

    VPUTC                                                             VPUTC
    
    
    
    PROTOTYPE:
    
        vputc(char chr)
    
    
    ARGUMENTS:
    
        chr     - Character to display
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function displays a character on  the  video  screen  at  the
       current cursor position.
    
          Characters are output in "tty" fashion, with  proper  handling  of
       control codes such as CARRIAGE-RETURN, LINE-FEED and BELL. The screen
       will scroll upwards when a NEWLINE is printed on the bottom  line  of
       the screen, or when the bottom line wraps around to the next.
    
          Although only the lower 8 bits of a passed value are used, "vputc"
       will not perform ANY output translations if any of the upper  8  bits
       are set. This provides a method of displaying  the  video  characters
       represented by control codes such as NEWLINE, and BACKSPACE.
    
          The external "char" variable "V_ATTR" may be used to set the video
       attribute used by "VPUTC" to display the  character.  This  value  is
       written to the attribute location associated with  the  character  on
       the video display hardware. Its effect  is  dependant  on  the  video
       adapter in use. The "video.h" header file contains definitions of the
       attribute bits for use on "standard" monochrome and color displays.
    
    
          "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        vputc(0x0A);            /* Line-feed, advance cursor */
        vputc(0x0A | 0xff00);   /* Display 0x0A character code */

    VPUTF                                                             VPUTF
    
    
    
    PROTOTYPE:
    
        vputf(char *string, int width)
    
    
    ARGUMENTS:
    
        string  - Pointer to character string
        width   - Width of output field
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "vputf" function outputs a  character  string  to  the  IBM-PC
       video screen using the video library functions.
    
          The string is left justified in a field of the specified width. If
       the string is shorter than "width", the field is padded with  blanks.
       If the string is longer than "width", the output is truncated.
    
          "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        vputf(message, 10); 

    VPUTS                                                             VPUTS
    
    
    
    PROTOTYPE:
    
        vputs(char *string)
    
    
    ARGUMENTS:
    
        string  - Pointer to character string
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "vputs" function outputs a  character  string  to  the  IBM-PC
       video screen using the video library functions.
    
          "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        vputs(message);

    VTSTC                                                             VTSTC
    
    
    
    PROTOTYPE:
    
        int vtstc()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        0       - No key pressed
        1-127   - ASCII value of key pressed
        < 0     - Special function key as defined in "video.h"
    
    
    DESCRIPTION:
    
          The "vtstc" function  tests  for  a  key  pressed  on  the  system
       console, and  returns  its  value.  A  returned  value  of  zero  (0)
       indicates that no key was found to be pressed.
    
          Note that due to the  buffering  of  the  IBM-PC  keyboard,  every
       keypress will be reported, even if the VTSTC function is called after
       a key is pressed and released.
    
    
    EXAMPLES:
    
        if(vtstc() == 0x1B) /* exit loop on ESCAPE key */
            break;

    VUPDATEXY                                                     VUPDATEXY
    
    
    
    PROTOTYPE:
    
        vupdatexy()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function updates the real X/Y cursor position  on  the  video
       screen to reflect the "logical" position  where  the  next  character
       will be output.
    
          The MICRO-C video library  uses  a  BIOS  interrupt  (INT  10)  to
       position the cursor, which is quite slow, compared to  the  speed  of
       the library video routines. To prevent this  from  slowing  down  the
       video output, the cursor is  only  physically  re-positioned  when  a
       "vgotoxy" or a "vgetc" is executed.
    
          This allows the library routines to run at full speed,  and  still
       put the cursor in the right place when  output  stops  and  an  input
       request is made.
    
          A side effect of this is that the cursor on the  screen  will  not
       appear to move unless  you  call  "vgotoxy"  or  "vgetc".  This  only
       affects the physical cursor on the screen, MICRO-C maintains its  own
       internal cursor location which it uses  to  determine  where  on  the
       screen the next write will occur.
    
          Some applications which run in  real  time  (Such  as  a  terminal
       emulator) do not call "vgetc", but use "vtstc" to poll  the  keyboard
       on a regular basis. In this case, the "vupdatexy" routine  should  be
       called any time that the visual position of the cursor is important.
    
          "VOPEN" MUST be called prior to using this function.
    
    
    EXAMPLES:
    
        vupdatexy();        /* position the cursor *
        c = vtstc();        /* Test for a character */

    MICRO-C Library                                                  Page: 4


    
                     +------------------------------------+
                     |                                    |
                     |  ********************************  |
                     |  * The IBM-PC WINDOWING library *  |
                     |  ********************************  |
                     |                                    |
                     +------------------------------------+
    
    
    
    
    
    
    
    
    
    
       1.3 IBM-PC WINDOWING Library
    
             The MICRO-C WINDOWING LIBRARY is a set of powerful, very  fast,
          compact, text based windowing functions for use with  the  MICRO-C
          compiler, on the IBM Personal Computer. Features  of  the  library
          include multiple open windows,  overlaid  windows  with  automatic
          save/restore  of  screen  underneath,  scrolling  within  windows,
          optional window borders, menu and form entry functions, and more.
    
             The library is organized into two parts, the first is a set  of
          assembly language routines which provides the  basic  "low  level"
          functions to open/close windows, and to output data in  them.  The
          second part of the library provides a set of 'C'  functions  which
          provide "high level"  functions  such  as  menu  and  form  entry,
          formatted printing, etc.

    MICRO-C Library                                                  Page: 5


          1.3.1 Window Control Block
    
                Whenever a new window is opened, the windowing library  sets
             up a WINDOW CONTROL  BLOCK  (WCB)  which  contains  information
             needed to access and control the window. The format of the  WCB
             is:
    
        Offset: 0   - Current video attribute *
                1   - Window flags (High 8 bits of w_open attrs) **
                2   - Absolute 'X' position of top left corner of
                      active region. ***
                3   - Absolute 'Y' position of top left corner of
                      active region. ***
                4   - Width in characters of active region ***
                5   - Height in characters of active region ***
                6   - Current 'X' cursor coordinate
                7   - Current 'Y' cursor coordinate
                8,9 - Pointer to previous window buffer
                10  - Previous cursor ENDING line
                11  - Previous cursor STARTING line
                12  - Previous cursor absolute 'X' position ****
                13  - Previous cursor absolute 'Y' position ****
                14..- Save area for SAVE/RESTORE function
    
        *       You may dynamically alter the video attribute of data
                written to the window by writing to this byte.
    
        **      You may dynamically alter the properties of the window by
                setting or clearing the flag bits with these exceptions:
                -DO NOT enable SAVE/RESTORE unless opened with it
                (It is Ok to disable SAVE/RESTORE).
                -DO NOT change the state of the BORDER bits.
    
        ***     For windows opened with a BORDER, this reflects the size
                of the active region (not including the border). Otherwise,
                this is the size of the entire window.
    
        ****    For full screen window which does not SAVE/RESTORE, you can
                set these values to zero to home cursor on exit.

    MICRO-C Library                                                  Page: 6


          1.3.2 External Variables
    
                In addition to  the  functions  decribed  on  the  following
             pages, the windowing library provides  the  following  external
             variables which may be accessed from within your 'C' program:
    
             1.3.2.1 W_BASE
    
                               extern int W_BASE;
    
                   This variable contains the  base  address  of  the  video
                screen, which may be used to determine the type  of  display
                present:
    
                        B000 = Monochrome
                        B800 = Color
    
    
             1.3.2.2 W_OPEN
    
                              extern char *W_OPEN;
    
                   This variable contains a  pointer  to  the  WCB  for  the
                "active" window, and controls which window is manipulated by
                certain library functions.  This  automatically  set  up  by
                "wopen" to point to the  last  window  opened,  but  may  be
                changed at any time with:
    
                                W_OPEN = window;
    
                   NOTE, when the active window is closed, W_OPEN  is  reset
                to point to the window which was active at the time that  it
                (the active window) was opened. If  windows  are  closed  in
                other than the reverse order  of  which  they  were  opened,
                W_OPEN may be left pointing to a window  which  has  already
                been closed. If this happens, YOU MUST NOT USE THE  "ACTIVE"
                WINDOW FUNCTIONS WITHOUT RESETTING W_OPEN  TO  POINT  TO  AN
                OPEN WINDOW. It is your (the programmer's) responsibility to
                insure that you know what window will  be  accessed  through
                W_OPEN at all times throughout your program.
    
          1.3.3 Window Library Functions
    
                The following pages contain a description of  each  function
             available in the IBM-PC windowing library.

    WCLEOL                                                           WCLEOL
    W_CLEOL                                                         W_CLEOL
    
    
    
    PROTOTYPE:
    
        wcleol()
        w_cleol(char *window)
    
    
    ARGUMENTS:
    
        window  - Pointer to WCB for an open window
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "wcleol" function clears the active window  from  the  current
       cursor position to the end of a line.
    
          The "w_cleol" function  clears  the  specified  window  fromt  the
       current position to the end of the line.
    
    
    EXAMPLES:
    
        wputs("Input> ");       /* Display a prompt */
        wcleol();               /* Clear remainder of input line */

    WCLEOW                                                           WCLEOW
    W_CLEOW                                                         W_CLEOW
    
    
    
    PROTOTYPE:
    
        wcleow()
        w_cleow(char *window)
    
    
    ARGUMENTS:
    
        window  - Pointer to WCB for an open window
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "wcleow" function clears the active window  from  the  current
       position to the end of the window.
    
          The "w_cleow"  function  clears  the  specified  window  from  the
       current position to the end of the window.
    
    
    EXAMPLES:
    
        wgotoxy(0, 10);         /* position at line 11 */
        wcleos();               /* Clear lower part of screen */

    WCLOSE                                                           WCLOSE
    W_CLOSE                                                         W_CLOSE
    
    
    
    PROTOTYPE:
    
        wclose()
        w_close(char *window)
    
    
    ARGUMENTS:
    
        window  - Pointer to WCB for an open window
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "wclose" function closes the "active" window, and de-activates
       it.
    
          The  "w_close"  function  closes   the   specified   window,   and
       de-activates it.
    
          If the window being closed is the "active"  window,  the  "active"
       window will revert to the window which was "active" at the time  that
       the window being closed was opened.
    
    
    EXAMPLES:
    
        wclose();       /* Close active window */
        w_close(title); /* Close the title window */

    WCLWIN                                                           WCLWIN
    W_CLWIN                                                         W_CLWIN
    
    
    
    PROTOTYPE:
    
        wclwin()
        w_clwin(char *window)
    
    
    ARGUMENTS:
    
        window  - Pointer to WCB for an open window
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "wclwin" function clears the entire active window  and  resets
       the cursor position to the top left hand corner.
    
          The "w_clwin" function clears the  entire  specified  window,  and
       resets the cursor position to the top left hand corner.
    
    
    EXAMPLES:
    
        if(c = 0x1b) {          /* Escape command */
            wclwin();           /* Clear the screen */
            wputs("Exiting back to main menu");
            return; }

    WCURSOR_BLOCK                                             WCURSOR_BLOCK
    
    
    
    PROTOTYPE:
    
        wcursor_block()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function enables (turns on) display of the cursor on the  IBM
       PC video display. The cursor is shown as  flashing  block,  occupying
       the entire character window.
    
    
    EXAMPLES:
    
        if(insert)              /* Test insert mode flag */
            wcursor_block();    /* Indicate inserting with block cursor */
        else
            wcursor_line();     /* Indicate overwrite with line cursor */

    WCURSOR_LINE                                               WCURSOR_LINE
    
    
    
    PROTOTYPE:
    
        wcursor_line()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function enables (turns on) display of the cursor on the  IBM
       PC video display. The cursor is shown as a single flashing  line,  at
       the bottom of the character window.
    
    
    EXAMPLES:
    
        wcursor_line();     /* Re-enable the cursor */
        exit(0);            /* And terminate */

    WCURSOR_OFF                                                 WCURSOR_OFF
    
    
    
    PROTOTYPE:
    
        wcursor_off()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This function inhibits (turns off) display of the  cursor  on  the
       IBM PC video display. This affects the cursor  display  only,  screen
       output will continue to be displayed at the correct cursor position.
    
    
    EXAMPLES:
    
        wclscr();           /* Clear screen */
        wcursor_off();      /* Inhibit cursor */
        wmenu(10, 10, 0x6007, main_menu, &index); /* Present main menu */

    WFORM                                                             WFORM
    
    
    
    PROTOTYPE:
    
        register wform(int x, int y, int attrs, char *prompts[],
                       char *strings,  ...)
    
    
    ARGUMENTS:
    
        x       - Absolute COLUMN of upper left corner of form window
        y       - Absolute ROW    of upper left corner of form window
        attrs   - Attributes for form window (See WOPEN)
        prompts - Prompt string for form entries
        strings - Destination string to receive form data
        ...     - Additional arguments may be required
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "wform" function opens  a  window,  which  contains  a  "form"
       consisting of prompts and data areas. Each data area is shown  beside
       its corresponding prompt, and may be edited using the keys  supported
       by WGETS. the UP and DOWN ARROW keys may be used to move the  editing
       cursor between the various fields in the input form.*
    
          The "attrs" argument contains the open attributes (see WOPEN)  for
       the menu window, and may  be  used  to  control  the  color,  border,
       clearing, etc.
    
          The "prompts" argument is an array of pointers to  strings,  which
       define the prompts and input  fields  in  the  form.  The  first  two
       characters of each string define the 'X' and 'Y'  coordinates  within
       the window of the prompt string. The  third  character  contains  the
       length of the destination string, and the  remainder  of  the  string
       contains the text prompt. The destination string is positioned in the
       window directly following the prompt string.  This  list  of  prompts
       must end with a NULL (0) element.
    
          The first (0) element of "prompts" does not actually point  to  an
       input definition, but contains the X and Y sizes for the window to be
       opened (High byte = X, Low byte = Y).
    
          Following the "prompts" argument, there must  be  one  destination
       "string" argument for each prompt defined. The strings must  be  long
       enough to contain the number of characters  specified  in  the  third
       byte of the coresponding "prompt" string.

          Only the lower seven bits of the field length are used  (length  =
       1-127), the high bit indicates that the field is to  contain  numbers
       only. In this case, the corresponding argument is NOT a pointer to  a
       string, but must be a pointer to an "int" variable.
    
          The form is exited by pressing the ESCAPE key.
    
    
    
    EXAMPLES:
    
        /* Sample input form */
            char *form[] = {
                50<<8|6,        /* Place in 50 by 6 window */
                "\x01\x00\x20Software  :",
                "\x01\x01\x20Author    :",
                "\x01\x02\x20Directory :",
                "\x01\x03\x20Filename  :",
                0 };
    
        /* Data areas for input form */
            char software[0x21] = "MICRO-C",
                author[0x21]    = "Dave Dunfield",
                direct[0x21]    = "C:\\MC",
                filename[0x21]  = "MC*.*";
    
        /* Simple main program to display the form */
        main()
        {
            wform(15, 9, 0xE007, form, software, author, direct, filename);
        }

    WGETC                                                             WGETC
    W_GETC                                                           W_GETC
    
    
    
    PROTOTYPE:
    
        int wgetc()
        int w_getc(char *window)
    
    
    ARGUMENTS:
    
        window  - Pointer to WCB for an open window
    
    
    RETURN VALUE:
    
        0-127   - ASCII value of key pressed
        < 0     - Special function key as defined in "window.h"
    
    
    DESCRIPTION:
    
          The "wgetc" function waits until a key is pressed  on  the  system
       console, and returns its value. The cursor is updated to be placed at
       the current cursor position in the active window.
    
          The "w_getc" function waits until a key is pressed on  the  system
       console, and returns its value. The cursor is updated to be placed at
       the current cursor position in the specified window.
    
          Note that due to the  buffering  of  the  IBM-PC  keyboard,  every
       keypress will be reported, even if the WGETC or  W_GETC  function  is
       called after a key is pressed and released.
    
    
    EXAMPLES:
    
        switch(wgetc()) {       /* Handle input keys
                . . .
        }

    WGETS                                                             WGETS
    
    
    
    PROTOTYPE:
    
        int wgets(int x, int y, char *string, int length)
    
    
    ARGUMENTS:
    
        x       - COLUMN position for input
        y       - ROW    position for input
        string  - Destination string
        length  - Length of string (High bit set = Numbers only)
    
    
    RETURN VALUE:
    
        Character causing exit
    
    
    DESCRIPTION:
    
          The "wgets" function positions the cursor at the specified X and Y
       coordinates, and displays the contents of "string"  (in  a  field  of
       "length" characters), and waits for input, which may be used to  edit
       the string.
    
          Any normal ASCII characters which are input will be  entered  into
       the string, The following function keys are recognized:
    
            LEFT ARROW          - Position cursor one space to the left
            RIGHT ARROW         - Position cursor one space to the right
            BACKSPACE           - Backup cursor & delete previous character
            DELETE              - Delete character under cursor
            INSERT              - Toggle between INSERT/OVERWRITE
            HOME                - Position cursor at start of string
            END                 - Position cursor at end of scring
            PAGE UP             - Clear entire field
            PAGE DOWN           - Clear from cursor to end of field
    
          Any other special function keys will cause "wgets"  to  terminate,
       and return the value of the offending key. (See  "window.h"  for  key
       definitions).
    
          When INSERT mode is enabled, all entered  text  will  be  inserted
       into the string, with the remainder of the  string  shifting  to  the
       right. This mode is indicated by a flashing BLOCK cursor.
    
          When OVERWRITE mode is enabled, all entered  text  will  overwrite
       the existing string. This  mode  is  indicated  by  a  flashing  LINE
       cursor.
    
    
    EXAMPLES:
    
        wgets(2, 5, name, 25);

    WGOTOXY                                                         WGOTOXY
    W_GOTOXY                                                       W_GOTOXY
    
    
    
    PROTOTYPE:
    
        wgotoxy(int x, int y)
        w_gotoxy(int x, int y, char *window)
    
    
    ARGUMENTS:
    
        x       - New COLUMN
        y       - New ROW
        window  - Pointer to WCB for an open window
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "wgotoxy" function positions  the  cursor  within  the  active
       window. Any further display output to that window will occur  at  the
       new ROW and COLUMN positions.
    
          The "w_gotoxy" function positions the cursor within the  specified
       window. Any further display output to that window will occur  at  the
       new ROW and COLUMN positions.
    
    
    EXAMPLES:
    
        for(i=0; i<10; ++i) {   /* Draw a diagonal line of 'X's */
            wgotoxy(i, i);
            wputc('X'); }

    WMENU                                                             WMENU
    
    
    
    PROTOTYPE:
    
        wmenu(int x, int y, int attrs, char *names[], int &index)
    
    
    ARGUMENTS:
    
        x       - Absolute COLUMN of top left corner of menu window
        y       - Absolute ROW    of top left corner of menu window
        attrs   - Attributes for menu window (see WOPEN)
        names   - Array to menu selection text (last entry = 0)
        index   - Address of message selection index variable
    
    
    RETURN VALUE:
    
        0   - Selection was made and ENTER pressed.
        !0  - Menu was aborted via ESCAPE key.
    
    
    DESCRIPTION:
    
          The "wmenu" function opens a window  containing  a  list  of  menu
       items at the specified ROW and COLUMN address. The user may  use  the
       UP, DOWN, HOME and END keys to select an entry by moving the  INVERSE
       VIDEO selection cursor. Pressing an alpha-numeric key  will  position
       the  selection  bar  to  the  first  entry  which  begins  with  that
       character.
    
          When the desired selection is under the cursor, the  selection  is
       made by pressing the ENTER key.
    
          At any time the menu selection may be  canceled  by  pressing  the
       ESCAPE key.
    
          The "attrs" argument contains the open attributes (see WOPEN)  for
       the menu window, and may  be  used  to  control  the  color,  border,
       clearing, etc.
    
          The "names" argument must be a pointer to an  array  of  character
       strings which are the selections to display. This array MUST end with
       a NULL (0) element to indicate the end of the list.
    
          The "index" argument is the address of  an  "int"  variable  which
       contains the position of the selection cursor. It controls where  the
       selection cursor will appear when the function is first invoked (0  =
       first entry), and also is assigned  the  position  of  the  selection
       cursor when the selection is made.
    
          Once a selection is made, the first character  of  that  selection
       will be hilighted in reverse video.

    
    
    
    
    EXAMPLES:
    
        char *names[] = { "One", "Two", "Three", "Four", "Five", 0 };
            . . .
        index = 0;
        if(wmenu(10, 10, 0xE007, names, &index))
            return;         /* Aborted, exit to higher level */
        switch(index) {     /* Handle selection */
            . . .
        }

    WOPEN                                                             WOPEN
    
    
    
    PROTOTYPE:
    
        char *wopen(int x, int y, int width, int height, int attrs)
    
    
    ARGUMENTS:
    
        x       - Absolute COLUMN of top left corner of window
        y       - Absolute ROW    of top left corner of window
        width   - The width of the window in characters
        height  - The height of the window in characters
        attrs   - The window attributes, BIT definitions:
                    15 - Enable SAVE/RESTORE screen under window
                *   14 - Enable SINGLE line BORDER
                *   13 - Enable DOUBLE line BORDER
                    12 - Enable CLEAR on OPEN
                **  11 - Enable CLEAR on CLOSE
                *** 10 - Disable NEWLINE (LF only)
                     9 - Enable SCROLLING in window
                     8 - Enable LINE WRAP in window
                   7-0 - Video attributes for window
    
            *   When BORDER is selected, window will include an enclosing
                BOX. In this case, the effective height and width of the
                active region (where text data can be written) will be
                reduced by 2.
    
            **  Has no visual effect when SAVE/RESTORE is enabled.
    
            *** If this BIT is set, CTRL-J will behave as LINEFEED only,
                and will not return the cursor to the left margin.
    
    RETURN VALUE:
    
        A pointer to the WCB for the newly opened window
        0 if the window could not be opened
    
    
    DESCRIPTION:
    
          The "wopen" function creates a new window on the PC video  screen.
       This newly created window is also made the "active" window, which  is
       automatically accessed by many of the windowing functions.
    
          If "wopen" is unable to allocate  enough  memory  for  the  window
       control block (WCB), it will fail and return a value of zero (0).
    
    
    EXAMPLES:
    
        /* Create a title window at top of screen */
        titlewin = wopen(0, 0, 80, 3, 0x6047);

    WPRINTF                                                         WPRINTF
    W_PRINTF                                                       W_PRINTF
    
    
    
    PROTOTYPE:
    
        register wprintf(char *format, arg, ...)
        register w_printf(char *window, char *format, arg, ...)
    
    
    ARGUMENTS:
    
        window  - Pointer to WCB for an open window
        format  - Pointer to format string
        arg     - Argument as determined by format string
        ...     - Additional arguments may be required
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "wprintf" function performs exactly as the  "PRINTF"  function
       in the standard function library, except that it outputs directly  to
       the active window using the low level windowing library functions.
    
          The "w_printf" function behaves similar to "wprintf", except  that
       the window to receive the output is specified as the first parameter.
    
          These functions should be used  in  preference  to  "PRINTF"  when
       using the windowing function library since "PRINTF" will not move the
       windowing librarys cursor, will not use the attributes from the  WCB,
       and will not respect the boundarys of the window.
    
          NOTE: This function uses a variable number of arguments, and  must
       be declared as "register" (See "window.h").
    
    
    EXAMPLES:
    
        wgotoxy(0, 0);
        wprintf("Window %u", screen);

    WPUTC                                                             WPUTC
    W_PUTC                                                           W_PUTC
    
    
    
    PROTOTYPE:
    
        wputc(int c)
        wputc(int c, char *window)
    
    
    ARGUMENTS:
    
        c       - Character to be written to window
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          This "wputc" function displays a character in the active window at
       the current cursor position.
    
          The "w_putc" functino displays a character in the specified window
       at the current cursor position.
    
          Characters are output in "tty" fashion, with  proper  handling  of
       control codes such as CARRIAGE-RETURN, LINE-FEED and BELL. The screen
       will scroll upwards when a NEWLINE is printed on the bottom  line  of
       the screen, or  when  the  bottom  line  wraps  around  to  the  next
       (Assuming those options are enabled in the window).
    
          Although only the lower 8 bits of a passed value are used, "vputc"
       will not perform ANY output translations if any of the upper  8  bits
       are set. This provides a method of displaying  the  video  characters
       represented by control codes such as NEWLINE, and BACKSPACE.
    
          The first byte of the window control block (WCB)  for  the  window
       contains the attributes which will be used to display the  character.
       This value is written to the attribute location associated  with  the
       character on the video display hardware. Its effect is  dependant  on
       the video  adapter  in  use.  The  "window.h"  header  file  contains
       definitions of the attribute bits for use  on  "standard"  monochrome
       and color displays.
    
    
    EXAMPLES:
    
        w_putc(0x0A, window1);      /* Line-feed, advance cursor */
        wputc(0x0A | 0xff00);       /* Display 0x0A character code */

    WPUTF                                                             WPUTF
    
    
    
    PROTOTYPE:
    
        wputf(char *string, int width)
    
    
    ARGUMENTS:
    
        string  - Pointer to character string
        width   - Width of output field
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "wputf" function outputs a  character  string  to  the  active
       window screen using the video library functions.
    
          The string is left justified in a field of the specified width. If
       the string is shorter than "width", the field is padded with  blanks.
       If the string is longer than "width", the output is truncated.
    
    
    EXAMPLES:
    
        wputf(message, 10); 

    WPUTS                                                             WPUTS
    W_PUTS                                                           W_PUTS
    
    
    
    PROTOTYPE:
    
        wputs(char *string)
        w_puts(char *string, char *window)
    
    
    ARGUMENTS:
    
        string  - Pointer to character string
        window  - Pointer to WCB for an open window
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "wputs" function outputs a  character  string  to  the  active
       window.
    
          The "w_puts" function output a character string to  the  specified
       window.
    
    
    EXAMPLES:
    
        wputs(message);
        w_puts(message, window1);

    WTSTC                                                             WTSTC
    W_TSTC                                                           W_TSTC
    
    
    
    PROTOTYPE:
    
        int wtstc()
        int w_tstc(char *window)
    
    
    ARGUMENTS:
    
        window  - Pointer to WCB for an open window
    
    
    RETURN VALUE:
    
        0       - No key pressed
        1-127   - ASCII value of key pressed
        < 0     - Special function key as defined in "window.h"
    
    
    DESCRIPTION:
    
          The "wtstc" function  tests  for  a  key  pressed  on  the  system
       console, and returns its value. If a character is found,  the  cursor
       is updated in the active window.
    
          The "w_tstc" function tests  for  a  key  pressed  on  the  system
       console, and returns its value. If a character is found,  the  cursor
       is updated in the specified window.
    
          A returned value of zero (0) indicates that no key was found to be
       pressed.
    
          Note that due to the  buffering  of  the  IBM-PC  keyboard,  every
       keypress will be reported, even if the WTSTC or  W_TSTC  function  is
       called after a key is pressed and released.
    
    
    EXAMPLES:
    
        if(wtstc() == 0x1B) /* exit loop on ESCAPE key */
            break;

    WUPDATEXY                                                     WUPDATEXY
    W_UPDATEXY                                                   W_UPDATEXY
    
    
    
    PROTOTYPE:
    
        wupdatexy()
        w_updatexy(char *window)
    
    
    ARGUMENTS:
    
        window  - Pointer to WCB for an open window
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "wupdatexy" function updates the real X/Y cursor  position  on
       the video screen to reflect the "logical"  position  where  the  next
       character will be output in the active window.
    
          The "w_updatexy" function updates the real X/Y cursor position  on
       the video screen to reflect the "logical"  position  where  the  next
       character will be output in the specified window.
    
          The MICRO-C Windowing library uses a BIOS interrupt  (INT  10)  to
       position the cursor, which is quite slow, compared to  the  speed  of
       the library video routines. To prevent this  from  slowing  down  the
       video output, the cursor is  only  physically  re-positioned  when  a
       "wgotoxy" or a "wgetc" is executed.
    
          This allows the library routines to run at full speed,  and  still
       put the cursor in the right place when  output  stops  and  an  input
       request is made.
    
          A side effect of this is that the cursor on the  screen  will  not
       appear to move unless  you  call  "wgotoxy"  or  "wgetc".  This  only
       affects the physical cursor on the screen, MICRO-C maintains its  own
       internal cursor location which it uses  to  determine  where  on  the
       screen the next write will occur.
    
          Some applications which run in  real  time  (Such  as  a  terminal
       emulator) do not call "wgetc", but use "wtstc" to poll  the  keyboard
       on a regular basis. In this case, the "wupdatexy" routine  should  be
       called any time that the visual position of the cursor is important.
    
    
    EXAMPLES:
    
        wupdatexy();        /* position the cursor *
        c = wtstc();        /* Test for a character */




                                MICRO-C Library

                               TABLE OF CONTENTS


                                                                         Page

     1. THE MICRO-C LIBRARIES                                               1

        1.1 STANDARD Library                                                2
        1.2 IBM-PC/MS-DOS Library                                           3
        1.3 IBM-PC WINDOWING Library                                        4