SERVILE SOFTWARE DECODER





                                  Version 2.7






                         Shareware Version Disk Manual







2
                                  DISCLAIMER



The Servile Software Decoder is supplied as a tool to assist in the reverse-
engineering of IBM PC software, with special attention to computer viruses. 
Because of the nature of the subject, no guarrantees can be made that a 
program analysed with SSD will behave in the same manner when executed outside 
of the SSD environment. 

Months of development and rigourous testing have gone into SSD, including 
testing it on hundreds of Shareware, freeware and commercial programs, 
including computer viruses. Some programs, by their nature, exhibit pecuiliar 
behaviour when analysed with SSD which they do not exhibit otherwise.

Use of SSD is at your own risk. The author accepts no liability in any form 
and makes no guarrantees as to the suitability of this product for any purpose 
what so ever. 



3
                                 INTRODUCTION





The Servile Software Decoder (SSD) is a powerful code and program analyser for 
the IBM PC. SSD is neither a disassembler nor a debugger, although it shares 
some similarities with both. Unlike a disassembler, SSD activately analyses 
the code of a program, this allows SSD to analyse encrypted programs, unlike a 
disassemler. Unlike a debugger, SSD interprets the program under analysis. 
This has the advantage that SSD is safe to use with computer viruses as 
dangerous commands are inhibited. It also implies that SSD is not prone to 
anti-debugger instructions which are often contained in computer viruses. 

Because SSD interprets programs, rather than passing them straight to DOS for 
execution, some programs may exhibit slightly different behaviour when 
analysed than when executed. This is unfortunately unavoidable.

When SSD starts execution, or loads a new file, the PC interrupt vector table 
is copied into memory. All subsequent reads and writes to the first 1024 bytes 
of RAM (vector table) are then redirected to the SSD copy of the interrupt 
vector table. This allows programs to think they have changed an interrupt  
vector, but at the same time retains security by not changing the real vector.


Animate            Record             Utility               File            Exit
                                                                                
ÉÍÍÍÍÍÍÍÍÍÍÍTraceÍÍÍÍÍÍÍÍÍÍÍÍËÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍAnalysisÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                       ÉÍÍÍÍÍÍÍÍÍÍÍÍAboutÍÍÍÍÍÍÍÍÍÍÍÍÍ»                       º
º                       º   Servile Software Decoder   º                       º
º                       º                              º                       º
º                       º         Version 2.7          º                       º
º                       º     (Shareware Version)      º                       º
º                       º                              º                       º
º                       º     Copyright (c)1994 by     º                       º
º                       º                              º                       º
º                       º       Servile Software       º                       º
º                       ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼                       º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
º  AX  0000   BX  0000   CX  0000   DX  0000   SI  0000   DI  0000   BP  0000  º
º  CS  53C8   DS  53B8   ES  53B8   SS  552C   SP  0080   IP  0000    0000000  º
º                                                                     ZCSOAPD  º
ÈÍÍÍÍÍÍÍÍÍRegistersÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


4
                                    DISPLAY



SSD uses two display pages. Page 0, the normal default DOS display page is 
used for output from the program being analysed. Page 1 is used for the SSD 
main display which is divided into the following component parts: Menu bar, 
containing drop-down menus of facilities. Code window, which displays the 
dissasembly of each instruction as it occurs. Analysis window, which displays 
analysis information about the running program and also data dumps when 
requested. And the registers window which displays the current contents of the 
CPU registers as they appear to the program being analysed. 



Animate            Record             Utility               File            Exit
                                                                                
ÉÍÍÍÍÍÍÍÍÍÍÍTraceÍÍÍÍÍÍÍÍÍÍÍÍËÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍAnalysisÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
º  AX  0000   BX  0000   CX  0000   DX  0000   SI  0000   DI  0000   BP  0000  º
º  CS  53C8   DS  53B8   ES  53B8   SS  552C   SP  0080   IP  0000    0000000  º
º                                                                     ZCSOAPD  º
ÈÍÍÍÍÍÍÍÍÍRegistersÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

5
                                  FACILITIES


This section describes the various facilities available from the drop-down 
menus. Each menu is tackled in turn, with the menu name shown in CAPITALS, 
followed by the facilities available from that menu.



ANIMATE:

The "ANIMATE" menu provides access to the various facilities for running the 
loaded program. In brief, the loaded program may be single stepped, run at 
maximum speed or traced at three different speeds. A program which is being 
traced or run may be stopped by pressing the Esc key. When single stepping a 
program only the next instruction is fetched and interpreted.


Animate            Record             Utility               File            Exit
ÉÍÍÍÍÍÍÍÍ»                                                                      
º Step   ºÍÍTraceÍÍÍÍÍÍÍÍÍÍÍÍËÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍAnalysisÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º Run    º                   º                                                 º
º Slow   º                   º                                                 º
º Medium º                   º                                                 º
º Fast   º                   º                                                 º
ÈÍÍÍÍÍÍÍÍ¼                   º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
º  AX  0000   BX  0000   CX  0000   DX  0000   SI  0000   DI  0000   BP  0000  º
º  CS  53C8   DS  53B8   ES  53B8   SS  552C   SP  0080   IP  0000    0000000  º
º                                                                     ZCSOAPD  º
ÈÍÍÍÍÍÍÍÍÍRegistersÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼



6
Step:

Single step the loaded program. Only the next instruction is interpreted, and 
then SSD returns to the ANIMATE menu.

Run:

Run the program at maximum speed. Only the analysis details are displayed.

Slow:

Trace the program slowly. As each instruction is fetched and interpreted, its 
dissamembly and analysis are displayed togther with the new contents of all 
the registers. However, should the program be in a loop command, only the 
effect upon the registers is displayed untill the loop finishes.

Medium:

Trace the program fairly slowly. As each instruction is fetched and 
interpreted, its dissamembly and analysis are displayed togther with the new 
contents of all the registers. However, should the program be in a loop 
command, only the effect upon the registers is displayed untill the loop 
finishes. 

Fast:

Trace the program quickly. As each instruction is fetched and interpreted, its 
dissamembly and analysis are displayed togther with the new contents of all 
the registers. However, should the program be in a loop command, only the 
effect upon the registers is displayed untill the loop finishes. 



7
RECORD:

Toggle which details will be echoed to an output file. The details are 
cumulative. Selecting an option low in the list will result in details higher 
in the list also being recorded. Selecting "Code & Regs" results in all 
details being recorded.

A tick (û) appears next to the currently selected level of recording.

SSD requires you to enter a name of a file to which the details will be 
echoed. If you want the details echoed to the printer enter the file name PRN. 
This can be useful for tracing code which destroys the display, such as 
tracing interrupt 10 for example. Notice that if the printer is switched off, 
off-line or out-of-paper SSD will continue regardless, but nothing will be 
echoed to the printer until the problem is resolved.


Animate            Record             Utility               File            Exit
                   ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»                                             
ÉÍÍÍÍÍÍÍÍÍÍÍTraceÍÍº ûNone        ºÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍAnalysisÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º                  º  Analysis    º                                            º
º                  º  Code        º                                            º
º                  º  Code & Regs º                                            º
º                  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼                                            º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
º  AX  0000   BX  0000   CX  0000   DX  0000   SI  0000   DI  0000   BP  0000  º
º  CS  53C8   DS  53B8   ES  53B8   SS  552C   SP  0080   IP  0000    0000000  º
º                                                                     ZCSOAPD  º
ÈÍÍÍÍÍÍÍÍÍRegistersÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
                                                                                
                                                                                

8
UTILITY:

Miscellaneous utility facilities.

About....: 

Displays information about SSD. After reading the information displayed, press 
any key to remove the "about" window from the display. 

Change Regs:

Allows any register value to be changed. Highlight the required register, and 
press return to enter a new value.

Trace Int:

Allows an interrupt to be specified instead of a program. To trace the 
interrupt use the ANIMATE facilities as for a program. (CS and IP are set to 
the values stored in the appropriate interrupt vector).

Dump:

Display the values in RAM at a specified segment:offset address. Registers may 
be specified for the address, eg: es:di is a valid address.

Output:

Display the program's output screen. Press a key to return to the analysis 
screen.

Interrupts:

Displays the values recorded in the interrupt vector table (SSD copy). To 
continue the listing press any key, pressing Esc will terminate the listing.


9
Animate            Record             Utility               File            Exit
                                      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍ»                           
ÉÍÍÍÍÍÍÍÍÍÍÍTraceÍÍÍÍÍÍÍÍÍÍÍÍËÍÍÍÍÍÍÍÍº About....   ºlysisÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º                            º        º Change Regs º                          º
º                            º        º Trace Int   º                          º
º                            º        º Dump        º                          º
º                            º        º Output      º                          º
º                            º        º Interrupts  º                          º
º                            º        ÈÍÍÍÍÍÍÍÍÍÍÍÍÍ¼                          º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
º  AX  0000   BX  0000   CX  0000   DX  0000   SI  0000   DI  0000   BP  0000  º
º  CS  53C8   DS  53B8   ES  53B8   SS  552C   SP  0080   IP  0000    0000000  º
º                                                                     ZCSOAPD  º
ÈÍÍÍÍÍÍÍÍÍRegistersÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


10
FILE:

Facilities for opening and writing program files and also for specifying 
command line arguments.

Open:

Allows you to specify a program to load.

Write:

Writes a memory image of the current .COM program to disk. Reports an error if 
the loaded program is a .EXE program.


Arguments:

Allows command line arguments to be specified. These are then passed to the 
program being analysed.

                                                                                
Animate            Record             Utility               File            Exit
                                                            ÉÍÍÍÍÍÍÍÍÍÍÍ»       
ÉÍÍÍÍÍÍÍÍÍÍÍTraceÍÍÍÍÍÍÍÍÍÍÍÍËÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍAnalysisÍÍº Open      ºÍÍÍÍÍÍ»
º                            º                              º Write     º      º
º                            º                              º Arguments º      º
º                            º                              ÈÍÍÍÍÍÍÍÍÍÍÍ¼      º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
º                            º                                                 º
ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
º  AX  0000   BX  0000   CX  0000   DX  0000   SI  0000   DI  0000   BP  0000  º
º  CS  53C8   DS  53B8   ES  53B8   SS  552C   SP  0080   IP  0000    0000000  º
º                                                                     ZCSOAPD  º
ÈÍÍÍÍÍÍÍÍÍRegistersÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


EXIT:

Returns to DOS

11
                              INHIBITED COMMANDS



SSD inhibits all attempts to disable hardware by writing to I/O ports, 
generation of audible tones, attempts to create new files, closing of the 
standard files; stdin, stdout, stderr, stdaux and stdprn, write to disk and 
disk formatting instructions. Instructions which attempt to write to memory 
occupied by SSD are also rejected. 

Inhibiting operations allows a greater degree of safety when analysing 
computer viruses, but has the disadvantage that subsequent program behaviour 
may be altered in some circumstances.

SSD inhibits attempts to change the following interrupt vectors:

08, 0A, 0B, 0C, 0D, 0E, 0F, 1C, 21, 24, 70

However, subsequent reads of these vectors will return a value as though the 
change had occured.

12
                                DOS ERROR CODES


DOS error codes are usually returned in the AX register following an abortive 
DOS interrupt call, usually indicated by a set carry flag.


Code    Meaning

 01     Invalid function
 02     File not found
 03     Path not found
 04     No handles available
 05     Access denied
 06     Invalid handle
 07     Memory control blocks destroyed
 08     Insufficient memory
 09     Invalid memory block address
 0A     Invalid environment
 0B     Invalid format
 0C     Invalid access code
 0D     Invalid data
 0F     Invalid drive
 10     Attempt to remove current directory
 11     Not the same device
 12     No more files
 13     Disk write-protected
 14     Unknown unit
 15     Drive not ready
 16     Unknown command
 17     CRC error
 18     Bad request structure length
 19     Seek error
 1A     Unknown media type
 1B     Sector not found
 1C     Out of paper
 1D     Write fault
 1E     Read fault
 1F     General failure
 20     Sharing violation
 21     Lock violation
 22     Invalid disk change
 23     FCB unavailable
 24     Sharing buffer overflow




13
                                  MEMORY MAP


The following table describes the layout of conventional RAM within the IBNM 
PC and compatibles. Each address is shown in the format segment:offset as is 
conventional with Intel's approach to memory addressing with the 8080 family 
of CPUs.



0000:0000               RAM
                        Vector Table
                        256 entries stored as segment word
                                               offset word

0040:0000               BIOS data area
    :0000               Base I/O address of 1st serial I/O port, zero if none
    :0002               Base I/O address of 2nd serial I/O port, zero if none
    :0004               Base I/O address of 3rd serial I/O port, zero if none
    :0006               Base I/O address of 4th serial I/O port, zero if none
    :0008               Base I/O address of 1st parallel I/O port, zero if none
    :000A               Base I/O address of 2nd parallel I/O port, zero if none
    :000C               Base I/O address of 3rd parallel I/O port, zero if none
    :000E               Base I/O address of 4th parallel port, zero if none
                        Segment of Extended BIOS Data Segment (PS/2)
    :0010               Installed hardware
    :0012               POST status
    :0013               Base memory size in kbytes (0-640)
    :0015               Manufacturing test scratch pad
    :0016               Manufacturing test scratch pad
                        BIOS control flags (PS/2 mod 30)
                        Keyclick loudness 00h-7Fh (Compaq Deskpro 386K)
    :0017               Keyboard status flags 1
    :0018               Keyboard status flags 2
    :0019               Keyboard: Alt-nnn keypad workspace
    :001A               Keyboard: ptr to next character in keyboard buffer
    :001C               Keyboard: ptr to first free slot in keyboard buffer
    :001E               Keyboard circular buffer 
    :003E               Diskette recalibrate status
    :003F               Diskette motor status
    :0040               Diskette motor turn-off time-out count
    :0041               Diskette last operation status
    :0042               XT: command byte to hard disk controller
                        AT: write precompensation cylinder number / 4
    :0043               XT: bit 5 = drive number, bits 3-0=head number
                        AT: sector count
    :0044               XT: bits 6,7 = high bits of track, bits 5-0 = start 
                            sector-1 
                        AT: starting sector
    :0045               low byte of track number
    :0046               XT: sector count
                        AT: high bits of track number
    :0047               XT: control byte from HD parameters (step rate,...)
                        AT: 101DHHHH, D=drive number, HHHH=head number

14
    :0048               XT: INT 13 subfunction number
                        AT: comand byte to hard disk controller
    :0049               Current video mode
    :004A               Video columns on screen
    :004C               Video page (regen buffer) size in bytes
    :004E               Video current page start address in regen buffer
    :0050               Video cursor position (col, row) for eight pages
    :0060               Video cursor type, hi=startline, lo=endline
    :0062               Video current page number
    :0063               Video CRT controller base address
    :0065               Video current setting of mode select register 
    :0066               Video current setting of CGA palette register 03D9h
    :0067               POST real mode re-entry point after certain resets
                        pointer to reset code upon system reset (PS/2 except 
                        mod 25,30) with memory preserved 
    :006B               POST last unexpected interrupt
    :006C               Timer ticks since midnight
    :0070               Timer overflow
    :0071               Ctrl-Break flag
    :0072               POST reset flag
    :0074               Fixed disk last operation status, except ESDI drives
    :0075               Number of fixed disk drives
    :0076               Fixed disk control byte   
    :0077               Fixed disk I/O port offset 
    :0078               Parallel devices 1-3 time-out counters
    :007B               parallel device 4 time-out counter (non-PS/2 and PS/2 
                        Mod 25,30)
    :007C               Serial devices 1-4 time-out counters
    :0080               Keyboard buffer start as offset from segment 40h 
    :0082               Keyboard buffer end+1 as offset from segment 40h 
    :0084               Video EGA/MCGA/VGA rows on screen minus one
    :0085               Video EGA/MCGA/VGA character height in scan-lines
    :0087               Video EGA/VGA control
    :0088               Video EGA/VGA switches
    :0089               Video MCGA/VGA mode-set option control
    :008A               Video MCGA/VGA index into Display Combination Code 
                        table
    :008B               Diskette media control (not XT)
    :008C               Fixed disk controller status (not XT)
    :008D               Fixed disk controller Error Status (not XT)
    :008E               Fixed disk Interrupt Control (not XT)
    :008F               Diskette controller information (not XT)
    :0090               Diskette drive 0 media state
    :0091               Diskette drive 1 media state
    :0092               Diskette drive 0 media state at start of operation
    :0093               Diskette drive 1 media state at start of operation
    :0094               Diskette drive 0 current track number
    :0095               Diskette drive 1 current track number
    :0096               Keyboard status byte 1
    :0097               Keyboard status byte 2
    :0098               Timer2
    :009C               Timer2
    :00A0               Timer2
    :00A1               LAN Support Program Interrupt Arbitrator present

15
    :00A2               Reserved for network adapters
    :00A4               Saved Fixed Disk Interrupt Vector (PS/2 Mod 30)
    :00A8               Video: EGA/MCGA/VGA ptr to Video Save Pointer Table 
    :00AC               Reserved
    :00B0               Vendor specific
    :00CE               Count of days since last boot
    :00D0               Reserved
    :00F0               Reserved for user
    :0100               Print Screen Status byte
    :010E               State of BREAK at start of BASICA.COM execution
    :010F               BASICA v2.10 running flag
    :0116               INT 1B at start of BASICA.COM execution
    :011A               INT 24 at start of BASICA.COM execution
0040:011E               DOS kernel
????:????               Device drivers
????:????               Resident part of COMMAND.COM
????:????               FREE SPACE
A000:0000               EGA/VGA Video RAM
B000:0000               Video RAM
C000:0000               EGA/VGA BIOS ROM extension
C000:8000               Hard drive ROM extension
E000:0000               Other BIOS ROM extensions
F000:0000               BIOS ROM
    :EFC7               Floppy disk parameters
    :F0A4               Video hardware table
    :FEF3               Initial interrupt vector table values
    :FFF5               BIOS version date code
    :FFFE               Model type 
    :FFFF               Model sub type 

16
                      XT, AT and PS/2  I/O port addresses


This data is provided for the purpose of providing an understanding into the 
nature of a program being analysed which accesses hardware ports. It is not 
intended to describe how to program the IBM PC hardware ports since this can 
lead to damage of the hardware. 


"r" indicates port may be read. "w" indicates port may be written. "r/w" 
indicates port may be both read and written.

0000-001F ----  DMA 1   (first Direct Memory Access controller 8237)

0000    r/w     DMA channel 0 address    byte 0, then byte 1.
0001    r/w     DMA channel 0 word count byte 0, then byte 1.
0002    r/w     DMA channel 1 address    byte 0, then byte 1.
0003    r/w     DMA channel 1 word count byte 0, then byte 1.
0004    r/w     DMA channel 2 address    byte 0, then byte 1.
0005    r/w     DMA channel 2 word count byte 0, then byte 1.
0006    r/w     DMA channel 3 address    byte 0, then byte 1.
0007    r/w     DMA channel 3 word count byte 0, then byte 1.

0008    r       DMA channel 0-3 status register
                 bit 7 = 1  channel 3 request
                 bit 6 = 1  channel 2 request
                 bit 5 = 1  channel 1 request
                 bit 4 = 1  channel 0 request
                 bit 3 = 1  channel terminal count on channel 3
                 bit 2 = 1  channel terminal count on channel 2
                 bit 1 = 1  channel terminal count on channel 1
                 bit 0 = 1  channel terminal count on channel 0

0008    w       DMA channel 0-3 command register
                 bit 7 = 1  DACK sense active high
                       = 0  DACK sense active low
                 bit 6 = 1  DREQ sense active high
                       = 0  DREQ sense active low
                 bit 5 = 1  extended write selection
                       = 0  late write selection
                 bit 4 = 1  rotating priority
                       = 0  fixed priority
                 bit 3 = 1  compressed timing
                       = 0  normal timing
                 bit 2 = 1  enable controller
                       = 0  enable memory-to-memory

0009    w       DMA write request register


17
000A    r/w     DMA channel 0-3 mask register
                 bit 7-3 = 0   reserved
                 bit 2   = 0   clear mask bit
                         = 1   set mask bit
                 bit 1-0 = 00  channel 0 select
                         = 01  channel 1 select
                         = 10  channel 2 select
                         = 11  channel 3 select

000B    w       DMA channel 0-3 mode register
                 bit 7-6 = 00  demand mode
                         = 01  single mode
                         = 10  block mode
                         = 11  cascade mode
                 bit 5   = 0   address increment select
                         = 1   address decrement select
                 bit 3-2 = 00  verify operation
                         = 01  write to memory
                         = 10  read from memory
                         = 11  reserved
                 bit 1-0 = 00  channel 0 select
                         = 01  channel 1 select
                         = 10  channel 2 select
                         = 11  channel 3 select

000C    w       DMA clear byte pointer flip-flop
000D    r       DMA read temporary register
000D    w       DMA master clear
000E    w       DMA clear mask register
000F    w       DMA write mask register


0010-001F ----  DMA controller (8237) on PS/2 model 60 & 80


0018    w       PS/2 extended function register

001A            PS/2 extended function execute


0020-003F ----  PIC 1   (Programmable Interrupt Controller 8259)

0020    w       PIC initialization command word ICW1
                 bit 7-5 = 0  only used in 80/85 mode
                 bit 4   = 1  ICW1 is being issued
                 bit 3   = 0  edge triggered mode
                         = 1  level triggered mode
                 bit 2   = 0  successive interrupt vectors use 8 bytes
                         = 1  successive interrupt vectors use 4 bytes
                 bit 1   = 0  cascade mode
                         = 1  single mode, no ICW3 needed
                 bit 0   = 0  no ICW4 needed
                         = 1  ICW4 needed


18
0021    w       PIC  ICW2,ICW3,ICW4 after ICW1 to 0020
                ICW2:
                 bit 7-3 = address lines A0-A3 of base vector address for PIC
                 bit 2-0 = reserved
                ICW3:
                 bit 7-0 = 0  slave controller not attached to corresponding
                              interrupt pin
                         = 1  slave controller attached to corresponding
                              interrupt pin
                ICW4:
                 bit 7-5 = 0  reserved
                 bit 4   = 0  no special fully-nested mode
                         = 1  special fully-nested mode
                 bit 3-2 = 0x nonbuffered mode
                         = 10 buffered mode/slave
                         = 11 buffered mode/master
                 bit 1   = 0  normal EOI
                         = 1  Auto EOI
                 bit 0   = 0  8085 mode
                         = 1  8086/8088 mode

0021    r/w     PIC master interrupt mask register
                OCW1:
                 bit 7 = 0  enable parallel printer interrupt
                 bit 6 = 0  enable diskette interrupt
                 bit 5 = 0  enable fixed disk interrupt
                 bit 4 = 0  enable serial port 1 interrupt
                 bit 3 = 0  enable serial port 2 interrupt
                 bit 2 = 0  enable video interrupt
                 bit 1 = 0  enable keyboard, mouse, RTC interrupt
                 bit 0 = 0  enable timer interrupt
                OCW2:
                 bit 7-5 = 000  rotate in auto EOI mode (clear)
                         = 001  nonspecific EOI
                         = 010  no operation
                         = 011  specific EOI
                         = 100  rotate in auto EOI mode (set)
                         = 101  rotate on nonspecific EOI command
                         = 110  set priority command
                         = 111  rotate on specific EOI command
                 bit 4   = 0    reserved
                 bit 3   = 0    reserved
                 bit 2-0        interrupt request to which the command applies

0020    r       PIC  interrupt request/in-service registers by OCW3
                request register:
                 bit 7-0 = 0  no active request for the corresponding int. line
                         = 1  active request for corresponding interrupt line
                in-service register:
                 bit 7-0 = 0  corresponding line not currently being serviced
                         = 1  corresponding int. line currently being serviced


19
0020    w       PIC OCW3
                 bit 7   = 0   reserved
                 bit 6-5 = 0x  no operation
                         = 10  reset special mask
                         = 11  set special mask
                 bit 4   = 0   reserved
                 bit 3   = 1   reserved
                 bit 2   = 0   no poll command
                         = 1   poll command
                 bit 1-0 = 0x  no operation
                         = 10  read int.request register on next read at 0020
                         = 11  read int.in-service register on next read 0020


0022-002B ----  Intel 82355, part of chipset for 386sx
                 initialisation in POST will disable these addresses,
                 only a hard reset will enable them again.

0022    r/w     82335 MCR memory configuration register
0024            82335 RC1 roll compare register
0026            82335 RC2 roll compare register
0028            82335 CC0 compare register
002A            82335 CC1 compare register

                  values for CC0 and CC1:
                  00F9,0000  enable range compare CC0 0-512K  CC1 disable
                  00F1,0000  enable range compare CC0 0-1024K CC1 disable
                  00F1,10F9  enable range compare CC0 0-1M    CC1 1M-1M5
                  00E1,0000  enable range compare CC0 0-2M    CC1 disable
                  00E1,0000  enable range compare CC0 0-2M    CC1 disable
                  00C1,0000  enable range compare CC0 0-4M    CC1 disable
                  00C1,40E1  enable range compare CC0 0-4M    CC1 4M-6M
                  0081,0000  enable range compare CC0 0-8M    CC1 disable


0040-005F ----  PIT  (Programmable Interrupt Timer  8253, 8254)
                 XT & AT uses 40-43    PS/2 uses 40, 42,43,44, 47

0040    r/w     PIT  counter 0, counter divisor       (XT, AT, PS/2)
0041    r/w     PIT  counter 1, RAM refresh counter   (XT, AT)
0042    r/w     PIT  counter 2, cassette & speaker    (XT, AT, PS/2)


20
0043    r/w     PIT  mode port, control word register for counters 0-2
                 bit 7-6 = 00  counter 0 select
                         = 01  counter 1 select   (not PS/2)
                         = 10  counter 2 select
                 bit 5-4 = 00  counter latch command
                         = 01  read/write counter bits 0-7 only
                         = 10  read/write counter bits 8-15 only
                         = 11  read/write counter bits 0-7 first, then 8-15
                 bit 3-1 = 000 mode 0 select
                         = 001 mode 1 select - programmable one shot
                         = x10 mode 2 select - rate generator
                         = x11 mode 3 select - square wave generator
                         = 100 mode 4 select - software triggered strobe
                         = 101 mode 5 select - hardware triggered strobe
                 bit 0   = 0   binary counter 16 bits
                         = 1   BCD counter

0044    r/w     PIT  counter 3 (PS/2, EISA)
                used as fail-safe timer. generates an NMI on time out.
                for user generated NMI see at 0462.

0047    w       PIT  control word register counter 3 (PS/2, EISA)
                 bit 7-6 = 00  counter 3 select
                         = 01  reserved
                         = 10  reserved
                         = 11  reserved
                 bit 5-4 = 00  counter latch command counter 3
                         = 01  read/write counter bits 0-7 only
                         = 1x  reserved
                 bit 3-0 = 00

0048            EISA
004A            EISA
004B            EISA



21
0060-006F ----  Keyboard controller (8041, 8042)  (or PPI (8255) on XT)
                 XT uses 60-63,  AT uses 60-64

                 AT keyboard controller input port bit definitions
                  bit 7   = 0  keyboard inhibited
                  bit 6   = 0  CGA, else MDA
                  bit 5   = 0  manufacturing jumper installed
                  bit 4   = 0  system RAM 512K, else 640K
                  bit 3-0      reserved

                 AT keyboard controller input port bit definitions by Compaq
                  bit 7   = 0  security lock is locked
                  bit 6   = 0  Compaq dual-scan display
                          = 1  non-Compaq display
                  bit 5   = 0  system board dip switch 5 is ON
                  bit 4   = 0  auto speed selected 
                          = 1  high speed selected
                  bit 3   = 0  slow (4MHz) 
                          = 1  fast (8MHz)
                  bit 2   = 0  80287 installed 
                          = 1  no NDP installed
                  bit 1-0      reserved

                 AT keyboard controller output port bit definitions
                  bit 7 =    keyboard data output
                  bit 6 =    keyboard clock output
                  bit 5 = 0  input buffer full
                  bit 4 = 0  output buffer empty
                  bit 3 =    reserved (see note)
                  bit 2 =    reserved (see note)
                  bit 1 =    gate A20
                  bit 0 =    system reset
                Note:   bits 2 and 3 are the turbo speed switch or password
                          lock on Award/AMI/Phoenix BIOSes.  These bits make
                          use of nonstandard keyboard controller BIOS
                          functionality to manipulate
                            pin 23 (8041 port 22) as turbo switch for AWARD
                            pin 35 (8041 port 15) as turbo switch/pw lock for
                                Phoenix

0060    r/w     KB controller data port or keyboard input buffer (ISA, EISA)
                should only be read from after status port bit0 = 1
                should only be written to if status port bit1 = 0
                keyboard commands (data goes also to port 0060):
                 ED     dbl   set/reset mode indicators Caps Num Scrl
                 EE     sngl  diagnostic echo. returns EE.
                 EF-F2  sngl  NOP (No OPeration). reserved for future use
                 F3     dbl   set typematic rate/delay
                 F4     sngl  enable keyboard
                 F5     sngl  disable keyboard. set default parameters
                 F6     sngl  set default parameters
                 F7-FD  sngl  NOP
                 FE     sngl  resend last scancode
                 FF     sngl  perform internal power-on reset function



22
0060    r       KeyBoard or KB controller data output buffer (via PPI on XT)

0061    w       KB controller port B (ISA, EISA)   (PS/2 port A is at 0092)
                system control port for compatibility with 8255
                 bit 7  (1= IRQ 0 reset )
                 bit 6-4    reserved
                 bit 3 = 1  channel check enable
                 bit 2 = 1  parity check enable
                 bit 1 = 1  speaker data enable
                 bit 0 = 1  timer 2 gate to speaker enable

0061    r       KB controller port B control register (ISA, EISA)
                system control port for compatibility with 8255
                 bit 7   parity check occurred
                 bit 6   channel check occurred
                 bit 5   mirrors timer 2 output condition
                 bit 4   toggles with each refresh request
                 bit 3   channel check status
                 bit 2   parity check status
                 bit 1   speaker data status
                 bit 0   timer 2 gate to speaker status

0061    w       PPI  Programmable Peripheral Interface 8255 (XT only)
                system control port
                 bit 7 = 1  clear keyboard
                 bit 6 = 0  hold keyboard clock low
                 bit 5 = 0  I/O check enable
                 bit 4 = 0  RAM parity check enable
                 bit 3 = 0  read low switches
                 bit 2      reserved, often used as turbo switch
                 bit 1 = 1  speaker data enable
                 bit 0 = 1  timer 2 gate to speaker enable

0062    r/w     PPI (XT only)
                 bit 7 = 1  RAM parity check
                 bit 6 = 1  I/O channel check
                 bit 5 = 1  timer 2 channel out
                 bit 4      reserved 
                 bit 3 = 1  system board RAM size type 1
                 bit 2 = 1  system board RAM size type 2
                 bit 1 = 1  coprocessor installed
                 bit 0 = 1  loop in POST


23
0063    r/w     PPI (XT only) command mode register  (read dipswitches)
                 bit 7-6 = 00  1 diskette drive
                         = 01  2 diskette drives
                         = 10  3 diskette drives
                         = 11  4 diskette drives
                 bit 5-4 = 00  reserved
                         = 01  40*25 color (mono mode)
                         = 10  80*25 color (mono mode)
                         = 11  MDA 80*25
                 bit 3-2 = 00  256K (using 256K chips)
                         = 01  512K (using 256K chips)
                         = 10  576K (using 256K chips)
                         = 11  640K (using 256K chips)
                 bit 3-2 = 00  64K  (using 64K chips)
                         = 01  128K (using 64K chips)
                         = 10  192K (using 64K chips)
                         = 11  256K (using 64K chips)
                 bit 1-0       reserved

0064    r       KB controller read status (ISA, EISA)
                 bit 7 = 1 parity error on transmission from keyboard
                 bit 6 = 1 receive timeout
                 bit 5 = 1 transmit timeout
                 bit 4 = 0 keyboard inhibit
                 bit 3 = 1 data in input register is command
                         0 data in input register is data
                 bit 2 = 0 system flag status 
                       = 0 power up or reset 
                       = 1 selftest OK
                 bit 1 = 1 input buffer full (input 60/64 has data for 8042)
                 bit 0 = 1 output buffer full (output 60 has data for system)

0064    r        KB controller read status by Compaq
                 bit 7 = 1 parity error detected (11-bit format only). If an
                           error is detected, a Resend command is sent to the
                           keyboard once only, as an attempt to recover.
                 bit 6 = 1 receive timeout. transmission didn't finish in 2mS.
                 bit 5 = 1 transmission timeout error
                            bit 5,6,7  cause
                                1 0 0  No clock
                                1 1 0  Clock OK, no response
                                1 0 1  Clock OK, parity error
                 bit 4 = 0 security lock engaged
                 bit 3 = 1 data in OUTPUT register is command
                         0 data in OUTPUT register is data
                 bit 2 = 0 system flag status 
                       = 0 power up or reset 
                       = 1 soft reset
                 bit 1 = 1 input buffer full (output 60/64 has data)
                 bit 0 = 0 no new data in buffer (input 60 has data)


24
0064    w       KB controller input buffer (ISA, EISA)
                KB controller commands (data goes to port 0060):
                 20     read  read byte zero of internal RAM, this is the
                              last KB command send to 8041
                      Compaq  Put current command byte on port 0060
                                command structure:
                                bit 7   reserved
                                bit 6 = 1 convert KB codes to 8086 scan codes
                                bit 5 = 0 use 11-bit codes 
                                      = 1 use 8086 codes
                                bit 4 = 0 enable keyboard 
                                      = 1 disable keyboard
                                bit 3 = 1 ignore security lock state
                                bit 2     this bit goes into bit2 status reg.
                                bit 1 = 0 reserved
                                bit 0 = 1 generate int. when output buffer full
                 21-3F  read  reads the byte specified in the lower 5 bits of
                              the command in the 8041's internal RAM
                 60-7F  dbl   writes the data byte to the address specified in
                              the 5 lower bits of the command.

                              Alternate description KB IO command 60 summary:
                               bit7 = 0 reserved
                               bit6 =   IBM PC compatibility mode
                               bit5 =   IBM PC mode
                               bit4 =   disable kb
                               bit3 =   inhibit override
                               bit2 =   system flag
                               bit1 = 0 reserved
                               bit0 =   enableoutput buffer full interrupt

                 60   Compaq  Load new command (60 to [64], command to [60])
                 A1   Compaq  unknown speedfunction 
                 A2   Compaq  unknown speedfunction 
                 A3   Compaq  Enable system speed control
                 A4   Compaq  Toggle speed
                 A5   Compaq  Special reed. the 8042 places the real values
                              of port 2 except for bits 4 and 5 wich are given
                              a new definition in the output buffer. No output
                              buffer full is generated.
                                if bit 5 = 0, a 9-bit keyboard is in use
                                if bit 5 = 1, an 11-bit keyboard is in use
                                if bit 4 = 0, outp-buff-full interrupt disabled
                                if bit 4 = 1, output-buffer-full int. enabled
                 A6   Compaq  unknown speedfunction 
                 AA     sngl  initiate self-test. will return 55 to data port
                      Compaq  Initializes ports 1 and 2, disables the keyboard
                              and clears the buffer pointers. It then places
                              55 in the output buffer.
                 AB     sngl  initiate interface test. result values:
                               0 = no error
                               1 = keyboard clock line stuck low
                               2 = keyboard clock line stuck high
                               3 = keyboard data line is stuck low

25
                               4 = keyboard data line stuck high
                      Compaq   5 = Compaq diagnostic feature
                 AC     read  diagnostic dump. the contents of the 8041 RAM,
                              output port, input port, status word are send.
                 AD     sngl  disable keyboard (sets bit 4 of commmand byte)
                 AE     sngl  enable keyboard  (resets bit 4 of commmand byte)
                 AF     AWARD Enhanced Command: read keyboard version
                 C0     read  read input port
                      Compaq  Places status of input port in output buffer. use
                              this command only when the output buffer is empty
                 C1     AWARD Enhanced Command: poll input port Low nibble
                 C2     AWARD Enhanced Command: poll input port High nibble
                 D0     read  read output port
                      Compaq  Places byte in output port in output buffer. use
                              this command only when the output buffer is empty
                 D1     dbl   write output port. next byte written  to 0060
                              will be written to the 8041 output port
                      Compaq  The system speed bits are not set by this command
                              use commands A1-A6 (!) for speed functions.
                 D2     AWARD Enhanced Command: write keyboard output buffer
                 D3     AWARD Enhanced Command: write pointing device out.buf.
                 D4     AWARD Enhanced Command: write to auxiliary device
                 DD     sngl  disable address line A20. default in Real Mode
                 DF     sngl  enable address line A20
                 E0     read  read test inputs. bit0 = T0 and bit1 = T1
                 Exx    AWARD Enhanced Command: active output port
                 ED   Compaq  This is a two part command to control the state
                              of the NumLock CpasLock and ScrollLock LEDs
                              The second byte contains the state to set LEDs.
                                bit 7-3    reserved. should be set to 0.
                                bit 2 = 0  Caps Lock LED off
                                bit 1 = 0  Num Lock LED off
                                bit 0 = 0  Scroll Lock LED off
                 F0-FF  sngl  pulse output port low for 6 microseconds.
                              bits 0-3 contain the mask for the bits to be
                              pulsed. a bit is pulsed if its mask bit is zero.
                              bit0=system reset. Don't set to zero. Pulse only!

0065    r       communications port (Olivetti M24)

0068    w       HP-Vectra  control buffer (HP commands)
0069    r       HP-Vectra  SVC (keyboard request SerViCe port)
006A    w       HP-Vectra  clear processing, done

006C-006F       HP-HIL  (Human Interface Link = async. serial inputs 0-7)


0070-007F ----  CMOS RAM/RTC (Real Time Clock  MC146818)


26
0070    w       CMOS RAM index register port (ISA, EISA)
                 bit 7   = 1  NMI disabled
                         = 0  NMI enabled
                 bit 6-0      CMOS RAM index (64 bytes, sometimes 128 bytes)

                any write to 0070 should be followed by an action to 0071
                or the RTC wil be left in an unknown state.

0071    r/w     CMOS RAM data port (ISA, EISA)
                RTC registers:
                00    current second in BCD
                01    alarm second   in BCD
                02    current minute in BCD
                03    alarm minute   in BCD
                04    current hour in BCD
                05    alarm hour   in BCD
                06    day of week  in BCD
                07    day of month in BCD
                08    month in BCD
                09    year  in BCD (00-99)
                0A    status register A
                       bit 7 = 1  update in progress
                       bit 6-4 divider that identifies the time-based
                                frequency
                       bit 3-0 rate selection output  frequency and int. rate
                0B    status register B
                       bit 7 = 0  run
                             = 1  halt
                       bit 6 = 1  enable periodic interrupt
                       bit 5 = 1  enable alarm interrupt
                       bit 4 = 1  enable update-ended interrupt
                       bit 3 = 1  enable square wave interrupt
                       bit 2 = 1  calendar is in binary format
                             = 0  calendar is in BCD format
                       bit 1 = 1  24-hour mode
                             = 0  12-hour mode
                       bit 0 = 1  enable daylight savings time. only in USA.
                                  useless in Europe. Some DOS versions clear
                                  this bit when you use the DAT/TIME command.
                0C    status register C
                       bit 7 =    interrupt request flag
                       bit 6 =    peridoc interrupt flag
                       bit 5 =    alarm interrupt flag
                       bit 4 =    update interrupt flag
                       bit 3-0    reserved
                0D    status register D
                       bit 7 = 1  Real-Time Clock has power
                       bit 6-0    reserved
                0E    diagnostics status byte
                       bit 7 = 0  RTC lost power
                       bit 6 = 1  CMOS RAM checksum bad
                       bit 5 = 1  invalid configuration information at POST
                       bit 4 = 1  memory size error at POST
                       bit 3 = 1  fixed disk/adapter failed initialization

27
                       bit 2 = 1  CMOS RAM time found invalid
                       bit 1 = 1  adapters do not match configuration (EISA)
                       bit 0 = 1  time out reading an adapter ID (EISA)
                0F    shutdown status byte
                       00 = normal execution of POST
                       01 = chip set initialization for real mode reentry
                       04 = jump to bootstrap code
                       05 = issue an EOI an JMP to Dword ptr at 40:67
                       06 = JMP to Dword ptrv at 40:67 without EOI
                       07 = return to INT15/87 (block move)
                       08 = return to POST memory test
                       09 = return to INT15/87 (block move)
                       0A = JMP to Dword ptr at 40:67 without EOI
                       0B = return IRETS through 40:67
                10    diskette drive type for A: and B:
                       bit 7-4  drive type of drive 0
                       bit 3-0  drive type of drive 1
                               = 0000      no drive
                               = 0001      360K
                               = 0010      1M2
                               = 0011      720K
                               = 0100      1M44
                               = 0101-1111 reserved
                11    reserved / AMI Extended CMOS setup (AMI Hi-Flex BIOS)
                       bit 7   = 1     Typematic Rate Programming
                       bit 6-5 = 00    Typematic Rate Delay 250 mSec
                       bit 4-0 = 00011 Typematic Rate 21.8 Chars/Sec
                12    fixed disk drive type for drive 0 and drive 1
                       bit 7-4  drive type of drive 0
                       bit 3-0  drive type of drive 1
                                if either of the nibbles equals 0F, then bytes
                                19 an 1A are valid
                13    reserved / AMI Extended CMOS setup (AMI Hi-Flex BIOS)
                       bit 7 = 1  Mouse Support Option
                       bit 6 = 1  Above 1 MB Memory Test disable
                       bit 5 = 1  Memory Test Tick Sound disable
                       bit 4 = 1  Memory Parity Error Check enable
                       bit 3 = 1  Hit <ESC> Message Display disabled
                       bit 2 = 1  Hard Disk Type 47 Data Area at address 0:300
                       bit 1 = 1  Wait For <F1> If Any Error enabled
                       bit 0 = 1  System Boot Up Num Lock is On
                14    equipment byte
                       bit 7-6   diskette drives installed
                               = 00  1 drive installed
                               = 01  2 drives installed
                               = 10  reserved
                               = 11  reserved
                       bit 5-4   primary display
                               = 00  adapter card with option ROM 
                               = 01  40*25 color
                               = 10  80*25 color
                               = 11  monochrome
                       bit 3-2   reserved
                       bit 1   = 1  coprocessor installed (non-Weitek)

28
                       bit 0        diskette drive avaliable for boot
                15    LSB of systemn base memory in Kb
                16    MSB of systemn base memory in Kb
                17    LSB of total extended memory in Kb
                18    MSB of total extended memory in Kb
                19    drive C extension byte
                1A    drive D extension byte
                1B-27 reserved
                1B/1C word to 82335 RC1 roll compare register at [24]
                      (Phoenix)
                1D/1E word to 82335 RC2 roll compare register at [26]
                      (Phoenix)
                28    HP-Vectra checksum over 29-2D
                29-2D reserved
                29/2A word to Intel 82335 CC0 compare register at [28]
                      (Phoenix)
                2B/2C word send to 82335 CC1 compare register at [2A]
                      (Phoenix)
                2D    AMI Extended CMOS setup (AMI Hi-Flex BIOS)
                      (Phoenix BIOS checks for the values AA or CC)
                       bit 7 = 1  Weitek Processor Absent
                       bit 6 = 1  Floppy Drive Seek At Boot disabled
                       bit 5 = 1  System Boot Up Sequence  C:, A:
                       bit 4 = 1  System Boot Up Speed is high
                       bit 3 = 1  Cache Memory enabled
                       bit 2 = 1  Internal Cache Memory  <1>
                       bit 1-0    reserved
                2E    CMOS MSB checksum over 10-2D
                2F    CMOS LSB checksum over 10-2D
                30    LSB of extended memory found above 1Mb at POST
                31    MSB of extended memory found above 1Mb at POST
                32    date century in BCD
                33    information flags
                       bit4 = bit4 from CPU register CR0   (Phoenix)
                              this bit is only known as INTEL RESERVED
                34-3F reserved  
                34     bit4 bit5 (Phoenix BIOS)
                3D/3E word to 82335 MCR memory config register at [22]
                      (Phoenix)
                3D     bit3      base memsize 512/640  (Phoenix)
                3E     bit7 = 1  relocate enable       (Phoenix)
                       bit1 = 1  shadow video enable   (Phoenix)
                       bit0 = 1  shadow BIOS enable    (Phoenix)


                User Definable Drive Parameters are also stored in CMOS RAM:

                AMI (386sx BIOS 1989) first user definable drive (type 47)
                 1B  L cylinders
                 1C  H cylinders
                 1D  heads
                 1E  L Write Precompensation Cylinder
                 1F  H Write Precompensation Cylinder
                 20  ??

29
                 21  L cylinders parking zone
                 22  H cylinders parking zone
                 23  sectors

                AMI (386sx BIOS 1989) second user definable drive (type 48)
                 24  L cylinders
                 25  H cylinders
                 26  heads
                 27  L Write Precompensation Cylinder
                 28  H Write Precompensation Cylinder
                 29  ??
                 2A  L cylinders parking zone
                 2B  H cylinders parking zone
                 2C  sectors

                Phoenix (386BIOS v1.10.03 1988) 1st user definable drv (type48)
                 20  L cylinders
                 21  H cylinders
                 22  heads
                 23  L Write Precompensation Cylinder
                 24  H Write Precompensation Cylinder
                 25  L cylinders parking zone
                 26  H cylinders parking zone
                 27  sectors

                Phoenix (386BIOS v1.10.03 1988) 2nd user definable drv (type49)
                (when PS/2-style password option is not used)
                 35  L cylinders
                 36  H cylinders
                 37  heads
                 38  L Write Precompensation Cylinder
                 39  H Write Precompensation Cylinder
                 3A  L cylinders parking zone
                 3B  H cylinders parking zone
                 3C  sectors

0078            HP-Vectra  Hard Reset: NMI enable/disable
                 bit 7 = 0  disable & clear hard reset from HP-HIL controller
                       = 1  enable hard reset from HP-HIL controller chip
                 bit 6-0    reserved


007C-007D ----  HP-Vectra  PIC 3   (Programmable Interrupt Controller 8259)
                cascaded to first controller.
                used for keyboard and input device interface.
007C    r/w     HP-Vectra  PIC 3  see at 0020  PIC 1
007D    r/w     HP-Vectra  PIC 3  see at 0021  PIC 1


0080    w       Manufacturing Diagnostics port



30
0080-008F ----  DMA page registers   (74612)

0080    r/w     extra page register (temporary storage)
0081    r/w     DMA channel 2 address byte 2
0082    r/w     DMA channel 3 address byte 2
0083    r/w     DMA channel 1 address byte 2
0084    r/w     extra page register
0085    r/w     extra page register
0086    r/w     extra page register
0087    r/w     DMA channel 0 address byte 2
0088    r/w     extra page register
0089    r/w     DMA channel 6 address byte 2
0089    r/w     DMA channel 7 address byte 2
0089    r/w     DMA channel 5 address byte 2
008C    r/w     extra page register
008D    r/w     extra page register
008E    r/w     extra page register
008F    r/w     DMA refresh page register


0090-009F ----  PS/2 POS (Programmable Option Select)

0090            Central arbitration control port
0091            Card selection feedback

0092    r/w     PS/2 system control port A  (port B is at 0061)
                 bit 7-6   any bit set to 1 turns activity light on
                 bit 5     reserved
                 bit 4 = 1 watchdog timout occurred 
                 bit 3 = 0 RTC/CMOS security lock (on password area) unlocked
                       = 1 CMOS locked (done by POST)
                 bit 2     reserved
                 bit 1 = 1 indicates A20 active
                 bit 0 = 0 system reset or write
                         1 pulse alternate reset pin (alternate CPU reset)

0094    w       system board enable/setup register
                 bit 7 = 1  enable functions
                       = 0  setup functions
                 bit 5 = 1  enables VGA
                       = 0  setup VGA

0095            reserved

0096    w       adapter enable /setup register
                 bit 3 = 1  setup adapters
                       = 0  enable registers

0097            reserved



31
00A0-00AF ----  PIC 2   (Programmable Interrupt Controller 8259)

00A0    r/w     NMI mask register (XT)

00A0    r/w     PIC 2  same as 0020 for PIC 1
00A1    r/w     PIC 2  same as 0021 for PIC 1 except for OCW1:
                 bit 7 = 0  reserved
                 bit 6 = 0  enable fixed disk interrupt
                 bit 5 = 0  enable coprocessor exception interrupt
                 bit 4 = 0  enable mouse interrupt
                 bit 3 = 0  reserved
                 bit 2 = 0  reserved
                 bit 1 = 0  enable redirect cascade
                 bit 0 = 0  enable real-time clock interrupt


00C0      ----  TI  SN746496 programmable tone/noise generator  PCjr


00C0-00DF ----  DMA 2   (second Direct Memory Access controller 8237)

00C0    r/w     DMA channel 4 memory address bytes 1 and 0 (low) (ISA, EISA)
00C2    r/w     DMA channel 4 transfer count bytes 1 and 0 (low) (ISA, EISA)
00C4    r/w     DMA channel 5 memory address bytes 1 and 0 (low) (ISA, EISA)
00C6    r/w     DMA channel 5 transfer count bytes 1 and 0 (low) (ISA, EISA)
00C8    r/w     DMA channel 6 memory address bytes 1 and 0 (low) (ISA, EISA)
00CA    r/w     DMA channel 6 transfer count bytes 1 and 0 (low) (ISA, EISA)
00CC    r/w     DMA channel 7 memory address byte 0 (low), then 1 (ISA, EISA)
00CE    r/w     DMA channel 7 transfer count byte 0 (low), then 1 (ISA, EISA)

00D0    r       DMA channel 4-7 status register (ISA, EISA)
                 bit 7 = 1  channel 7 request
                 bit 6 = 1  channel 6 request
                 bit 5 = 1  channel 5 request
                 bit 4 = 1  channel 4 request
                 bit 3 = 1  terminal count on channel 7
                 bit 2 = 1  terminal count on channel 6
                 bit 1 = 1  terminal count on channel 5
                 bit 0 = 1  terminal count on channel 4

00D0    w       DMA channel 4-7 command register (ISA, EISA)
                 bit 7 = 1  DACK sense active high
                       = 0  DACK sense active low
                 bit 6 = 1  DREQ sense active high
                       = 0  DREQ sense active low
                 bit 5 = 1  extended write selection
                       = 0  late write selection
                 bit 4 = 1  rotating priority
                       = 0  fixed priority
                 bit 3 = 1  compressed timing
                       = 0  normal timing
                 bit 2 = 0  enable controller
                 bit 1 = 1  enable memory-to-memory transfer
                 bit 0      .....


32
00D2    w       DMA channel 4-7 write request register (ISA, EISA)

00D4    w       DMA channel 4-7 write single mask register (ISA, EISA)
                 bit 7-3      reserved
                 bit 2   = 0  clear mask bit
                         = 1  set mask bit
                 bit 1-0 = 00 channel 4 select
                         = 01 channel 5 select
                         = 10 channel 6 select
                         = 11 channel 7 select

00D6    w       DMA channel 4-7 mode register (ISA, EISA)
                 bit 7-6 = 00  demand mode
                         = 01  single mode
                         = 10  block mode
                         = 11  cascade mode
                 bit 5   = 0   address increment select
                         = 1   address decrement select
                 bit 4   = 0   autoinitialisation disable
                         = 1   autoinitialisation enable
                 bit 3-2 = 00  verify operation
                         = 01  write to memory
                         = 10  read from memory
                         = 11  reserved
                 bit 1-0 = 00  channel 4 select
                         = 01  channel 5 select
                         = 10  channel 6 select
                         = 11  channel 7 select

00D8    w       DMA channel 4-7 clear byte pointer flip-flop (ISA, EISA)
00DA    r       DMA channel 4-7 read temporary register (ISA, EISA)
00DA    w       DMA channel 4-7 master clear (ISA, EISA)
00DC    w       DMA channel 4-7 clear mask register (ISA, EISA)
00DE    w       DMA channel 4-7 write mask register (ISA, EISA)

00E0            split address register, memory encoding registers PS/2m80 only


00F0-00F5 ----  PCjr Disk Controller

00F0            disk controller
00F2            disk controller control port
00F4            disk controller status register
00F5            disk controller data port


00F0-00FF ----  coprocessor (8087..80387)

00F0            math coprocessor clear busy latch
00F1            math coprocessor reset
00F8-00FF       math coprocessor


0100-010F ----  CompaQ Tape drive adapter. alternate address at 0300



33
0100-0107 ----  PS/2 POS (Programmable Option Select)

0100    r       POS register 0  Low adapter ID byte
0101    r       POS register 1  High adapter ID byte

0102    r/w     POS register 2  option select data byte 1
                 bit 0 is card enable (CDEN)

0103    r/w     POS register 3  option select data byte 2
0104    r/w     POS register 4  option select data byte 3
0105    r/w     POS register 5  option select data byte 4
                 bit 7  channel active (-CHCK)
                 bit 6  channel status

0106    r/w     POS register 6  Low subaddress extension
0107    r/w     POS register 7  High subaddress extension


0108-010F ----  8 digit LED info panel on IBM PS/2

010F    w       leftmost character on display
010E    w       second character
....    w
0108    w       eighth character


0130-013F ----  CompaQ SCSI adapter. alternate address at 0330


0130-0133 ----  Adaptec 154xB/154xC SCSI adapter.
                alternate address at 0134, 0230, 0234 ,0330 and 0334


0134-0137 ----  Adaptec 154xB/154xC SCSI adapter.
                alternate address at 0130, 0230, 0234 ,0330 and 0334


0140-014F ----  SCSI (alternate Small Computer System Interface) adapter
                (1st at 0340-034F)


0140-0157 ----  RTC (alternate Real Time Clock for XT)   (1st at 0340-0357)


0170-0177 ----  HDC 2   (2nd Fixed Disk Controller)   same as 01Fx (ISA, EISA)


01E8-01EF ----  System Control. Laptop chipset: Headland HL21 & Acer M5105

01ED    r/w     select internal register. Data to/from 01EF
01EE    r
01EF    r/w     reg.
                5  = 1000xxxx  for low CPU clock speed (4MHz on Morse/Mitac)
                   = 0xxxxxxx  for high CPU clock speed (16MHz on Morse/Mitac)



34
01F0-01F7 ----  HDC 1   (1st Fixed Disk Controller)   same as 017x (ISA, EISA)

01F0    r/w     data register

01F1    r       error register
                diagnostic mode errors:
                 bit 7-3        reserved
                 bit 2-1 = 001  no error detected
                         = 010  formatter device error
                         = 011  sector buffer error
                         = 100  ECC circuitry error
                         = 101  controlling microprocessor error
                 operation mode:
                  bit 7  = 1  bad block detected
                         = 0  block OK
                  bit 6  = 1  uncorrectable ECC error
                         = 0  no error
                  bit 5       reserved
                  bit 4  = 1  ID found
                         = 0  ID not found
                  bit 3       reserved
                  bit 2  = 1  command completed
                         = 0  command aborted
                  bit 1  = 1  track 000 not found
                         = 0  track 000 found
                  bit 0  = 1  DAM not found
                         = 0  DAM found (CP-3022 always 0)

01F1    w       WPC/4  (Write Precompensation Cylinder divided by 4)

01F2    r/w     sector count
01F3    r/w     sector number
01F4    r/w     cylinder low
01F5    r/w     cylinder high

01F6    r/w     drive/head
                 bit 7   = 1
                 bit 6   = 0
                 bit 5   = 1
                 bit 4   = 0  drive 0 select
                         = 1  drive 1 select
                 bit 3-0      head select bits

01F7    r       status register
                 bit 7 = 1  controller is executing a command
                 bit 6 = 1  drive is ready
                 bit 5 = 1  write fault
                 bit 4 = 1  seek complete
                 bit 3 = 1  sector buffer requires servicing
                 bit 2 = 1  disk data read successfully corrected
                 bit 1 = 1  index - set to 1 each disk revolution
                 bit 0 = 1  previous command ended in an error


35
01F7    w       command register
                commands:
                 98 E5   check power mode       (IDE)
                 90      execute drive diagnostics
                 50      format track
                 EC      identify drive         (IDE)
                 97 E3   idle                   (IDE)
                 95 E1   idle immediatete       (IDE)
                 91      initialize drive parameters
                 1x      recalibrate
                 E4      read buffer            (IDE)
                 C8      read DMA with retry    (IDE)
                 C9      read DMA without retry (IDE)
                 C4      read multiplec         (IDE)
                 20      read sectors with retry
                 21      read sectors without retry
                 22      read long with retry
                 23      read long without retry
                 40      read verify sectors with retry
                 41      read verify sectors without retry
                 7x      seek
                 EF      set features           (IDE)
                 C6      set multiple mode      (IDE)
                 99 E6   set sleep mode         (IDE)
                 96 E2   standby                (IDE)
                 94 E0   standby immediate      (IDE)
                 E8      write buffer           (IDE)
                 CA      write DMA with retry   (IDE)
                 CB      write DMA with retry   (IDE)
                 C5      write multiple         (IDE)
                 E9      write same             (IDE)
                 30      write sectors with retry
                 31      write sectors without retry
                 32      write long with retry
                 33      write long without retry
                 3C      write verify           (IDE)
                 9A      vendor unique          (IDE)
                 C0-C3   vendor unique          (IDE)
                 8x      vendor unique          (IDE)
                 F0-F4   EATA standard          (IDE)
                 F5-FF   vendor unique          (IDE)



36
0200-020F ----  Game port reserved I/O address space  
0200-0207 ----  Game port, eight identical addresses on some boards

0201    r       read joystick position and status
                 bit 7  status B joystick button 2 / D paddle button
                 bit 6  status B joystick button 1 / C paddle button
                 bit 5  status A joystick button 2 / B paddle button
                 bit 4  status A joystick button 1 / A paddle button
                 bit 3  B joystick Y coordinate    / D paddle coordinate
                 bit 2  B joystick X coordinate    / C paddle coordinate
                 bit 1  A joystick Y coordinate    / B paddle coordinate
                 bit 0  A joystick X coordinate    / A paddle coordinate

        w       fire joysticks four one-shots


0210-0217 ----  Expansion unit (XT)

0210    w       latch expansion bus data
        r       verify expansion bus data
0211    w       clear wait, test latch
        r       High byte data address
0212    r       Low byte data address
0213    w       0=enable,  1=disable expansion unit
0214    w       latch data  (receiver card port)
        r       read data   (receiver card port)
0215    r       High byte of address, then Low byte   (receiver card port)


0220-0227 ----  Soundblaster PRO and SSB 16 ASP


0220-022F ----  Soundblaster PRO 2.0


0220-022F ----  Soundblaster PRO 4.0
0220    r       left FM status port
0220    w       left FM music register address port (index)
0221    r/w     left FM music data port
0222    r       right FM status port
0222    w       right FM music register address port (index)
0223    r/w     right FM music data port
0224    w       mixer register address port (index)
0225    r/w     mixer data port
0226    w       DSP reset
0228    r       FM music status port
0228    w       FM music register address port (index)
0229    w       FM music data port
022A    r       DSP read data (voice I/O and Midi)
022C    w       DSP write data / write command
022C    r       DSP write buffer status (bit 7)
022E    r       DSP data available status (bit 7)

                The FM music is accessible on 0388/0389 for compatibility.



37
0230-0233 ----  Adaptec 154xB/154xC SCSI adapter.
                alternate address at 0130, 0134, 0230, 0330 and 0334


0234-0237 ----  Adaptec 154xB/154xC SCSI adapter.
                alternate address at 0130, 0134, 0230 ,0330 and 0334


0240-0257 ----  RTC (alternate Real Time Clock for XT)   (1st at 0340-0357)
                (used by TIMER.COM v1.2 which is the 'standard' timer program)


0258-025F ----  Intel Above Board


0278-027E ----  parallel printer port, same as 0378 and 03BC

0278    w       data port
0279    r/w     status port
027A    r/w     control port


02A2-02A3 ----  MSM58321RS clock


02B0-02BF ----  Trantor SCSI adapter


02B0-02DF ----  alternate EGA,  primary EGA at 03C0


02C0-02Cx ----  AST-clock


02E0-02EF ----  GPIB (General Purpose Interface Bus, IEEE 488 interface)
                (GAB 0 on XT)
02E1            GPIB (adapter 0)
02E2
02E3


02E0-02EF ----  data aquisition  (AT)

02E2            data aquisition (adapter 0)
02E3            data aquisition (adapter 0)


02E8-02EF ----  serial port, same as 02F8, 03E8, and 03F8



38
02F8-02FF ----  serial port, same as 02E8, 02F8, and 03F8

02F8    w       transmitter holding register
02F8    r       receiver buffer register
        r/w     divisor latch, low byte   when DLAB=1
02F9    r/w     divisor latch, high byte  when DLAB=1
        r/w     interrupt enable register when DLAB=0
02FA    r       interrupt identification register
02FB    r/w     line control register
02FC    r/w     modem control register
02FD    r       line status register
02FF    r/w     scratch register


0300-0301 ---- Soundblaster 16 ASP MPU-Midi


0300-031F ----  prototype cards
                Periscope hardware debugger


0300-030F ----  Philips CD-ROM player CM50
0310-031F ----  Philips CD-ROM player CM50


0320-0323 ----  XT HDC 1   (Hard Disk Controller)

0320    r/w     data register

0321    w       reset controller
        r       read controller hardware status
                 bit 7-6 = 0
                 bit 5        logical unit number
                 bit 4-2 = 0
                 bit 1   = 0  no error
                 bit 0   = 0 

0322    r       read DIPswitch setting on XT controller card
        w       generate controller-select pulse
0323    w       write pattern to DMA and INT mask register

0324-0327 ----  XT HDC 2   (Hard Disk Controller)
0328-032B ----  XT HDC 3   (Hard Disk Controller)
032C-032F ----  XT HDC 4   (Hard Disk Controller)


0330-0331 ----  MIDI interface


0330-0333 ----  Adaptec 154xB/154xC SCSI adapter. default address.
                alternate address at 0130, 0134, 0230, 0234 and 0334


0330-033F ----  CompaQ SCSI adapter. alternate address at 0130



39
0330-033F ----  Philips CD-ROM player CM50


0334-0337 ----  Adaptec 154xB/154xC SCSI adapter.
                alternate address at 0130, 0134, 0230 ,0234 and 0330


0338      ----  AdLib soundblaster card


0340-034F ----  Philips CD-ROM player CM50


0340-034F ----  SCSI (1st Small Computer System Interface) adapter
                (alternate at 0140-014F)


0340-0357 ----  RTC (1st Real Time Clock for XT), (alternate at 0240-0257)
                (used by TIMER.COM v1.2 which is the 'standard' timer program)

0340    r/w     0.01 seconds  0-99
0341    r/w     0.1 seconds   0-99
0342    r/w     seconds       0-59
0343    r/w     minutes       0-59
0343    r/w     hours         0-23
0345    r/w     day of week   1-7
0346    r/w     day of month  1-31
0347    r/w     month         1-12
0348
0349    r/w     year          0-99
034A
034B
034C
034D
034E
034F
0350    r       status?
0351    
0352
0353
0354    r       status?
0355
0356
0357


0348-0357 ----  DCA 3278


0360-036F ----  PC network (AT)
0360-0367 ----  PC network (XT only)



40
0370-0377 ----  FDC 2  (2nd Floppy Disk Controller 8272)  same as 03F0

0372    w       diskette controller DOR (Digital Output Register)
0374    r       diskette controller status register
0375    r/w     diskette controller data register
0376    r/w     FIXED disk controller data register
0377    r       diskette controller DIR (Digital Input Register)
0377    w       select register for diskette data transfer rate


0378-037A ----  parallel printer port, same as 0278 and 03BC

0378    w       data port
0379    r/w     status port
037A    r/w     control port


0380-038F ----  2nd Binary Synchronous Data Link Control adapter (see 03A0)

0380    r/w      on board 8255 port A, internal/external sense
0381    r/w      on board 8255 port B, external modem interface
0382    r/w      on board 8255 port C, internal control and gating
0383    r/w      on board 8255 mode register
0384    r/w      on board 8253 channel square wave generator
0385    r/w      on board 8253 channel 1 inactivity time-out
0386    r/w      on board 8253 channel 2 inactivity time-out
0387    r/w      on board 8253 mode register
0388    r/w      on board 8273 read: status  write: command
0389    r/w      on board 8273 read: response  write: parameter
038A    r/w      on board 8273 transmit interrupt status
038B    r/w      on board 8273 receiver interrupt status
038C    r/w      on board 8273 data


0388-0389 ---- Soundblaster PRO FM-Chip
0388-038B ---- Soundblaster 16 ASP FM-Chip


0390-039F ----  Cluster adapter (AT)

0390-0393       (adapter 0)     (XT)



41
03A0-03AF ----  1st SDLC (Binary Synchronous Data Link Control adapter)

0380    r/w      on board 8255 port A, internal/external sense
0381    r/w      on board 8255 port B, external modem interface
0382    r/w      on board 8255 port C, internal control and gating
0383    r/w      on board 8255 mode register
0384    r/w      on board 8253 counter 0 unused
0385    r/w      on board 8253 channel 1 inactivity time-out
0386    r/w      on board 8253 channel 2 inactivity time-out
0387    r/w      on board 8253 mode register
0388    r/w      on board 8251 data
0389    r/w      on board 8251 command/mode/status register


03B0-03BF ----  MDA  (Monochrome Display Adapter based on 6845)

03B0            same as 03B4
03B1            same as 03B5
03B2            same as 03B4
03B3            same as 03B5
03B4    w       MDA CRT index register   (EGA/VGA)
                selects which register (0-11h) is to be accessed through 3B5
03B5    r/w     MDA CRT data register    (EGA/VGA)
                selected by port 3B4. registers C-F may be read
                 00  horizontal total
                 01  horizontal displayed
                 02  horizontal sync position
                 03  horizontal sync pulse width
                 04  vertical total
                 05  vertical displayed
                 06  vertical sync position
                 07  vertical sunc pulse width
                 08  interlace mode
                 09  maximum scan lines
                 0A  cursor start
                 0B  cursor end
                 0C  start address high
                 0D  start address low
                 0E  cursor location high
                 0F  cursor location low
                 10  light pen high
                 11  light pen low
03B6            same as 03B4
03B7            same as 03B5
03B8    r/w     MDA mode control register
                 bit 7 not used
                 bit 6 not used
                 bit 5 enable blink
                 bit 4 not used
                 bit 3 video enable
                 bit 2 not used
                 bit 1 not used
                 bit 0 high resolution mode


42
03B9            reserved for color select register on color adapter

03BA    r       CRT status register      EGA/VGA: input status 1 register
                 bit 7-4 reserved
                 bit 3   black/white video
                 bit 2-1 reserved
                 bit 0   horizontal drive

                 bit 7   (MSD says) if this bit changes within 8000h reads then
                 bit 6-4 = 000 adapter is Hercules or compatible
                         = 001 adapter is Hercules+
                         = 101 adapter is Hercules InColor
                         else  adapter is unknown

03BA    w       EGA/VGA feature control register

03BB            reserved for light pen strobe reset


03BC-03BF ----  parallel printer port, same as 0278 and 0378

03BC    w       data port
03BD    r/w     status port
                 bit 7 = 0  busy
                 bit 6 = 0  acknowledge
                 bit 5 = 1  out of paper
                 bit 4 = 1  printer is selected
                 bit 3 = 0  error
                 bit 2 = 0  IRQ has occurred
                 bit 1-0    reserved

03BE    r/w     control port
                 bit 7-5    reserved
                 bit 4 = 1  enable IRQ
                 bit 3 = 1  select printer
                 bit 2 = 0  initialize printer
                 bit 1 = 1  automatic line feed
                 bit 0 = 1  strobe


03BF    r/w     Hercules configuration switch register
                 bit 7-2
                 bit 1 = 0  disables upper 32K of graphics mode buffer
                         1  enables upper 32K of graphics mode buffer
                 bit 0 = 0  prevents graphics mode
                         1  allows graphics mode



43
03C0-03CF ----  EGA  (1st Enhanced Graphics Adapter)    alternate at 02C0

03C0    (r)/w   EGA VGA ATC index/data register
03C1    r       VGA     other attribute register
03C2    r       EGA VGA input status 0 register
        w       VGA     miscellaneous output register
03C3    r/w     VGA     video subsystem enable
03C4    w       EGA     TS index register
        r/w     VGA     sequencer index register
03C5    w       EGA     TS data register
        r/w     VGA     other sequencer register
03C6    r/w     VGA     PEL mask register
03C7    r/w     VGA     PEL address read mode
        r       VGA     DAC state register
03C8    r/w     VGA     PEL address write mode
03C9    r/w     VGA     PEL data register
03CA    w       EGA     graphics 2 position register
        r       VGA     feature control register
03CC    w       EGA     graphics 1 position register
        r       VGA     miscellaneous output register
03CE    w       EGA     GDC index register
        r/w     VGA     graphics address register
03CF    w       EGA     GDC data register
        r/w     VGA     other graphics register


03D0-03DF ----  CGA   (Color Graphics Adapter)

03D0            same as 03D4
03D1            same as 03D5
03D2            same as 03D4
03D3            same as 03D5
03D4    w       CRT (6845) index register   (EGA/VGA)
                selects which register (0-11h) is to be accessed through 3B5
03D5    w       CRT (6845) data register    (EGA/VGA)
                selected by port 3B4. registers C-F may be read
                 (for registers see at 3B5)
03D6            same as 03D4
03D7            same as 03D5
03D8    r/w     CGA mode control register  (except PCjr)
                 bit 7-6      not used
                 bit 5   = 1  blink enabled
                 bit 4   = 1  640*200 graphics mode
                 bit 3   = 1  video enabled
                 bit 2   = 1  monochrome signal
                 bit 1   = 0  text mode
                         = 1  320*200 graphics mode
                 bit 0   = 0  40*25 text mode
                         = 1  80*25 text mode


44
03D9    r/w     CGA palette register
                 bit 7-6      not used
                 bit 5   = 0 active color set: red, green brown
                         = 1 active color set: cyan, magenta, white
                 bit 4       intense colors in graphics, background colors text
                 bit 3       intense border in 40*25, intense background in
                             320*200, intense foreground in 640*200
                 bit 2       red border in 40*25, red background in 320*200,
                             red foreground in 640*200
                 bit 1       green border in 40*25, green background in
                             320*200, green foreground in 640*200
                 bit 0       blue border in 40*25, blue background in 320*200,
                             blue foreground in 640*200

03DA    r       CGA status register     EGA/VGA: input status 1 register
                 bit 7-4     not used
                 bit 3 = 1   in vertical retrace
                 bit 2 = 1   light pen switch is off
                 bit 1 = 1   positive edge from light pen has set trigger
                 bit 0 = 0   do not use memory
                       = 1   memory access without interfering with display

03DA    w       EGA/VGA feature control register

03DB    w       clear light pen latch
03DC    r/w     preset licht pen latch

03DF            CRT/CPU page register  PCjr only


03E8-03EF ----  serial port, same as 02E8, 02F8, and 03F8


03F0-03F7 ----  FDC 1  (1st Floppy Disk Controller 8272)  same as 0370

03F0            diskette controller status A (PS/2)
                 bit 7   interrupt pending
                 bit 6   second drive installed
                 bit 5   step
                 bit 4   track 0
                 bit 3   head 1 select
                 bit 2   index
                 bit 1   write protect
                 bit 0   direction

03F1    r       diskette controller status B (PS/2)
                 bit 7-6  reserved
                 bit 5    drive select (0=A:, 1=B:)
                 bit 4    write data
                 bit 3    read data
                 bit 2    write enable
                 bit 1    motor enable 1
                 bit 0    motor enable 0


45
03F2    w       diskette controller DOR (Digital Output Register)
                 bit 7-6    reserved PS/2
                 bit 7 = 1  drive 3 motor enable
                 bit 6 = 1  drive 2 motor enable
                 bit 5 = 1  drive 1 motor enable
                 bit 4 = 1  drive 0 motor enable
                 bit 3 = 1  diskette DMA enable (reserved PS/2)
                 bit 2 = 1  FDC enable  (controller reset)
                       = 0  hold FDC at reset
                 bit 1-0    drive select (0=A 1=B ..)

03F4    r       diskette controller status register
                 bit 7 = 1  data register is ready
                 bit 6 = 1  transfer is from controller to system
                         0  transfer is from system to controller
                 bit 5 = 1  non-DMA mode
                 bit 4 = 1  diskette controller busy
                 bit 3 = 1  drive 3 busy (reserved on PS/2)
                 bit 2 = 1  drive 2 busy (reserved on PS/2)
                 bit 1 = 1  drive 1 busy
                 bit 0 = 1  drive 0 busy

03F5    r       diskette command status register 0
                 bit 7-6      last command status
                         = 00 command terminated successfully
                         = 01 command terminated abnormally
                         = 10 invalid command
                         = 11 terminated abnormally by change in ready signal
                 bit 5   = 1  seek completed
                 bit 4   = 1  equipment check occurred after error
                 bit 3   = 1  not ready
                 bit 2   = 1  head number at interrupt
                 bit 1-0 = 1  unit select (0=A 1=B .. )
                              (on PS/2  01=A  10=B)

                status register 1
                 bit 7      end of cylinder; sector# greater then sectors/track
                 bit 6 = 0
                 bit 5 = 1  CRC error in ID or data field
                 bit 4 = 1  overrun
                 bit 3 = 0
                 bit 2 = 1  sector ID not found
                 bit 1 = 1  write protect detected during write
                 bit 0 = 1  ID address mark not found

                status register 2
                 bit 7 = 0
                 bit 6 = 1  deleted Data Eddress Mark detected
                 bit 5 = 1  CRC error in data
                 bit 4 = 1  wrong cylinder detected
                 bit 3 = 1  scan command equal condition satisfied
                 bit 2 = 1  scan command failed, sector not found
                 bit 1 = 1  bad cylinder, ID not found
                 bit 0 = 1  missing Data Address Mark 


46
                status register 3
                 bit 7      fault status signal
                 bit 6      write protect status
                 bit 5      ready status
                 bit 4      track zero status
                 bit 3      two sided status signal
                 bit 2      side select (head select)
                 bit 1-0    unit select (0=A 1=B .. )

03F6    r/w     FIXED disk controller data register
                 bit 7-4    reserved
                 bit 3 = 0  reduce write current
                         1  head select 3 enable
                 bit 2 = 1  disk reset enable
                         0  disk reset disable
                 bit 1 = 0  disk initialization enable
                         1  disk initialization disable
                 bit 0      reserved

03F7    r       diskette controller DIR (Digital Input Register)
                 bit 7 = 1 diskette change

                 bit 6     FIXED DISK write gate
                 bit 5     FIXED DISK head select 3 / reduced write current
                 bit 4     FIXED DISK head select 2
                 bit 3     FIXED DISK head select 1
                 bit 2     FIXED DISK head select 0
                 bit 1     FIXED DISK drive 1 select
                 bit 0     FIXED DISK drive 0 select   conflicts with:

                 bit 0     diskette high density select

03F7    w       select register for diskette data transfer rate
                 bit 7-2       reserved
                 bit 1-0 = 00  500 Kb/S mode
                         = 01  300 Kb/S mode
                         = 10  250 Kb/S mode
                         = 11  reserved


03F8-03FF ----  serial port (8250,8251,16450,16550), same as 02E8,02F8,and 03F8

03F8    w       serial port, transmitter holding register, which contains the
                character to be sent. Bit 0 is sent first.
                 bit 7-0   data bits when DLAB=0 (Divisor Latch Access Bit)
        r       receiver buffer register, which contains the received character
                Bit 0 is received first
                 bit 7-0   data bits when DLAB=0 (Divisor Latch Access Bit)
        r/w     divisor latch low byte when DLAB=1


47
03F9    r/w     divisor latch high byte when DLAB=1
        r/w     interrupt enable register when DLAB=0
                 bits 7-4   reserved
                 bit 3 = 1  modem-status interrupt enable
                 bit 2 = 1  receiver-line-status interrupt enable
                 bit 1 = 1  transmitter-holding-register empty interrupt enable
                 bit 0 = 1  received-data-avail.int. enable (and 16550 timeout)

              - 16550 will interrupt if data exists in the FIFO and isn't read
                within the time it takes to receive four bytes or if no data is
                received within the time it takes to receive four bytes

03FA    r       interrupt identification register. Information about a pending
                interrupt is stored here. When the ID register is addressed,
                the highest priority interrupt is held, and no other interrupts
                are acknowledged until the CPU services that interrupt.
                 bit 7-6 = 00  reserved on 8250, 8251, 16450
                         = 11  if FIFO queues are enabled (16550 only)
                 bit 5-4 = 0 reserved
                 bit 3   = 0 reserved  8250, 16450
                         = 1 16550  timeout int. pending
                 bit 2-1 identify pending interrupt with the highest priority
                         = 11  receiver line status interrupt. 
                               priority = highest
                         = 10  received data available register interrupt. 
                               priority = second 
                         = 01  transmitter holding register empty interrupt. 
                               priority = third 
                         = 00  modem status interrupt. 
                               priority = fourth
                 bit 0   = 0   interrupt pending. Contents of register can be 
                               used as a pointer to the appropriate 
                               interrupt service routine 
                         = 1   no interrupt pending

             - interrupt pending flag uses reverse logic, 0 = pending, 1 = none
             - interrupt will occur if any of the line status bits are set
             - THRE bit is set when THRE register is emptied into the TSR



48
03FA    w       16650 FCR  (FIFO Control Register)
                 bit 7-6 = 00  1 byte
                         = 01  4 bytes
                         = 10  8 bytes
                         = 11 14 bytes
                 bit 5-4 = 00 reserved
                 bit 3   = 1  change RXRDY  TXRDY pins from mode 0 to mode 1
                 bit 2   = 1  clear XMIT FIFO
                 bit 1   = 1  clear RCVR FIFO
                 bit 0   = 1  enable clear XMIT and RCVR FIFO queues

              - bit 0 must be set in order to write to other FCR bits
              - bit 1 when set  the RCVR FIFO is cleared and this bit is reset
                the receiver shift register is not cleared
              - bit 2 when set  the XMIT FIFO is cleared and this bit is reset
                the transmit shift register is not cleared

03FB    r/w     line control register
                 bit 7 = 1  divisor latch access bit (DLAB)
                         0  receiver buffer, transmitter holding, or interrupt
                            enable register access
                 bit 6 = 1  set break enable. serial ouput is forced to spacing
                            state and remains there.
                 bit 5 =    stick parity
                 bit 4 = 1  even parity select
                 bit 3 =    parity enable
                         1  even number of ones are sent and checked in the 
                            data word bits and parity bit
                         0  odd number of ones are sent and checked
                 bit 2 = 0  one stop bit
                         1  zero stop bit
                 bit 1-0 00 word length is 5 bits
                         01 word length is 6 bits
                         10 word length is 7 bits
                         11 word length is 8 bits

03FC    r/w     modem control register
                 bit 7-5 = 0  reserved
                 bit 4 = 1  loopback mode for diagnostic testing of serial port
                            output of transmitter shift register is looped back
                            to receiver shift register input. In this mode
                            transmitted data is received immediately so that
                            the CPU can verify the transmit data/receive data
                            serial port paths.
                 bit 3 = 1  auxiliary user-designated output 2
                 bit 2 = 1  auxiliary user-designated output 1
                 bit 1 = 1  force request-to-send active
                 bit 0 = 1  force data-terminal-ready active


49
03FD    r       line status register
                 bit 7 = 0  reserved
                 bit 6 = 1  transmitter shift and holding registers empty
                 bit 5 = 1  transmitter holding register empty. Controller is
                            ready toaccept a new character to send.
                 bit 4 = 1  break interrupt. the received data input is held in
                            in the zero bit state longer than the time of start
                            bit + data bits + parity bit + stop bits.
                 bit 3 = 1  framing error. the stop bit that follows the last
                            parity or data bit is a zero bit.
                 bit 2 = 1  parity error. Character has wrong parity
                 bit 1 = 1  overrun error. a character was sent to the receiver
                            buffer before the previous character in the buffer
                            could be read. This destroys the previous
                            character.
                 bit 0 = 1  data ready. a complete incoming character has been
                            received and sent to the receiver buffer register.

03FE    r       modem status register
                 bit 7 = 1  data carrier detect
                 bit 6 = 1  ring indicator
                 bit 5 = 1  data set ready
                 bit 4 = 1  clear to send
                 bit 3 = 1  delta data carrier detect
                 bit 2 = 1  trailing edge ring indicator
                 bit 1 = 1  delta data set ready
                 bit 0 = 1  delta clear to send

              - bits 0-3 are reset when the CPU reads the MSR
              - bit 4 is the Modem Control Register RTS during loopback test
              - bit 5 is the Modem Control Register DTR during loopback test
              - bit 6 is the Modem Control Register OUT1 during loopback test
              - bit 7 is the Modem Control Register OUT2 during loopback test

03FF    r/w     scratch register

Adresses above 03FF apply to EISA machines only

                         1000-1FFF      slot 1 EISA
                         2000-2FFF      slot 2 EISA
                         3000-3FFF      slot 3 EISA
                         4000-4FFF      slot 4 EISA
                         5000-5FFF      slot 5 EISA
                         6000-6FFF      slot 6 EISA
                         7000-7FFF      slot 7 EISA


0401-04D6 ----  used by EISA systems only

0401    r/w     DMA channel 0 word count byte 2 (high)
0403    r/w     DMA channel 1 word count byte 2 (high)
0405    r/w     DMA channel 2 word count byte 2 (high)
0407    r/w     DMA channel 3 word count byte 2 (high)


50
040A    w       extended DMA chaining mode register, channels 0-3
                 bit 7-5      reserved
                 bit 4   = 0  generates IRQ13
                         = 1  generates terminal count
                 bit 3   = 0  do not start chaining
                         = 1  programming complete
                 bit 2   = 0  disable buffer chaining mode (default)
                         = 1  enable buffer chaining mode
                 bit 1-0      DMA channel select

040A    r       channel interrupt (IRQ13) status register
                 bit 7-5  interrupt on channels 7-5
                 bit 4    reserved
                 bit 3-0  interrupt on channels 3-0

040B    w       DMA extended mode register for channels 3-0.
                bit settings same as 04D6
                 bit 7   = 0  enable stop register
                 bit 6   = 0  terminal count is an output for this channel
(default)
                 bit 5-4      DMA cycle timing
                         = 00 ISA-compatible (default)
                         = 01 type A timing mode
                         = 10 type B timing mode
                         = 11 burst DMA mode
                 bit 3-2      Address mode
                         = 00 8-bit I/O, count by bytes (default)
                         = 01 16-bit I/O, count by words, address shifted
                         = 10 32-bit I/O, count by bytes
                         = 11 16-bit I/O, count by bytes
                 bit 1-0      DMA channel select


0461    r/w     Extended NMI status/control register
                 bit 7 = 1  NMI pending from fail-safe timer (read only)
                 bit 6 = 1  NMI pending from bus timeout NMI status (read
only)
                 bit 5 = 1  NMI pending (read only)
                 bit 4      reserved
                 bit 3 = 1  bus timeout NMI enable (read/write)
                 bit 2 = 1  fail-safe NMI enable (read/write)
                 bit 1 = 1  NMI I/O port enable (read/write)
                 bit 0      RSTDRV. bus reset (read/write)
                       = 0  normal bus reset operation
                       = 1  reset bus asserted

0462    w       Software NMI register. writing to this register causes an NMI
                if NMI's are enabled
                 bit 7 = 1  generates an NMI


51
0464    r       bus master status latch register (slots 1-8). identifies the
                last bus master that had control of the bus
                 bit 7 = 0  slot 8 had control last
                 bit 6 = 0  slot 7 had control last
                 bit 5 = 0  slot 6 had control last
                 bit 4 = 0  slot 5 had control last
                 bit 3 = 0  slot 4 had control last
                 bit 2 = 0  slot 3 had control last
                 bit 1 = 0  slot 2 had control last
                 bit 0 = 0  slot 1 had control last

0465    r       bus master status latch register (slots 9-16)
                 bit 7 = 0  slot 16 had control last
                 bit 6 = 0  slot 15 had control last
                 bit 5 = 0  slot 14 had control last
                 bit 4 = 0  slot 13 had control last
                 bit 3 = 0  slot 12 had control last
                 bit 2 = 0  slot 11 had control last
                 bit 1 = 0  slot 10 had control last
                 bit 0 = 0  slot 9  had control last


0481    r/w     DMA channel 2 address byte 3 (high)
0482    r/w     DMA channel 3 address byte 3 (high)
0483    r/w     DMA channel 1 address byte 3 (high)
0487    r/w     DMA channel 0 address byte 3 (high)
0489    r/w     DMA channel 6 address byte 3 (high)
048A    r/w     DMA channel 7 address byte 3 (high)
048B    r/w     DMA channel 5 address byte 3 (high)

04C6    r/w     DMA channel 5 word count byte 2 (high)
04CA    r/w     DMA channel 6 word count byte 2 (high)
04CE    r/w     DMA channel 7 word count byte 2 (high)


04D0    w       IRQ 0-7 interrupt edge/level registers
                 bit 7 = 1  IRQ 7 is level sensitive
                 bit 6 = 1  IRQ 6 is level sensitive
                 bit 5 = 1  IRQ 5 is level sensitive
                 bit 4 = 1  IRQ 4 is level sensitive
                 bit 3 = 1  IRQ 3 is level sensitive
                 bit 2-0    reserved

04D1    w       IRQ 8-15 interrupt edge/level registers
                 bit 7 = 1  IRQ 15 is level sensitive
                 bit 6 = 1  IRQ 14 is level sensitive
                 bit 5 = 1  reserved
                 bit 4 = 1  IRQ 12 is level sensitive
                 bit 3 = 1  IRQ 11 is level sensitive
                 bit 2 = 1  IRQ 10 is level sensitive
                 bit 1 = 1  IRQ 9  is level sensitive
                 bit 0      reserved


52
04D4    w       extended DMA chaining mode register, channels 4-7
                 bit 7-5 = 0  reserved
                 bit 4   = 0  generates IRQ 13
                         = 1  generates terminal count
                 bit 3   = 0  do not start chaining
                         = 1  programming complete
                 bit 2   = 0  disable buffer chaining mode (default)
                         = 1  enable buffer chaining mode
                 bit 1-0      DMA channel select

04D6    w       DMA extended mode register for channels 4-7
                bit settings same as 04B
                 bit 7   = 0  enable stop register
                 bit 6   = 0  terminal count is an output for this channel
(default)
                 bit 5-4      DMA cycle timing
                         = 00 ISA-compatible (default)
                         = 01 type A timing mode
                         = 10 type B timing mode
                         = 11 burst DMA mode
                 bit 3-2      Address mode
                         = 00 8-bit I/O, count by bytes (default)
                         = 01 16-bit I/O, count by words, address shifted
                         = 10 32-bit I/O, count by bytes
                         = 11 16-bit I/O, count by bytes
                 bit 1-0      DMA channel select


0601    w       System control. Laptop chipset: Headland HL21 & Acer M5105
                 bit 7 = 1  power led on
                 bit 6 = 1  LCD backlight off
                 bit 5
                 bit 4
                 bit 3
                 bit 2 = 1  video chips disabled, screen blanked.
                 bit 1
                 bit 0 = 1  will lock up your machine!

        r        =04        (always reads back this value)


0620-0627 ----  PC network (adapter 1)
0628-062F ----  PC network (adapter 2)


06E2-06E3 ----  data aquisition (adapter 1)


0790-0793 ----  cluster (adapter 1)


0800-08FF ----  I/O port access registers for extended CMOS RAM or SRAM
                (256 bytes at a time)
                Sometimes plain text can be seen here.



53
0A20-0A23 ----  Token Ring (adapter 1)
0A24-0A27 ----  Token Ring (adapter 2)


0AE2-0AE3 ----  cluster (adapter 2)
0B90-0B93 ----  cluster (adapter 2)


0C00    r/w     page register to write to SRAM or I/O


0C80-0C83 ----  system board ID registers


1390-1393 ----  cluster (adapter 3)


2100-210F ----  IBM XGA (eXtended Graphics Adapter  8514/A)
2110-211F ----  IBM XGA (eXtended Graphics Adapter  8514/A)
2120-212F ----  IBM XGA (eXtended Graphics Adapter  8514/A)
2130-213F ----  IBM XGA (eXtended Graphics Adapter  8514/A)
2140-214F ----  IBM XGA (eXtended Graphics Adapter  8514/A)
2150-215F ----  IBM XGA (eXtended Graphics Adapter  8514/A)
2160-216F ----  IBM XGA (eXtended Graphics Adapter  8514/A)
2170-217F ----  IBM XGA (eXtended Graphics Adapter  8514/A)


2390-2393 ----  cluster (adapter 4)


3220-3227 ----  serial port 3, description same as 03F8
3228-322F ----  serial port 4, description same as 03F8


3540-354F ----  IBM SCSI (Small Computer System Interface) adapter
3550-355F ----  IBM SCSI (Small Computer System Interface) adapter
3560-356F ----  IBM SCSI (Small Computer System Interface) adapter
3570-357F ----  IBM SCSI (Small Computer System Interface) adapter


4220-4227 ----  serial port, description same as 03F8
4228-422F ----  serial port, description same as 03F8


42E0-42EF ----  GPIB (General Purpose Interface Bus, IEEE 488 interface)

42E1    r/w     GPIB (adapter 2)


5220-5227 ----  serial port, description same as 03F8
5228-522F ----  serial port, description same as 03F8


62E0-62EF ----  GPIB (General Purpose Interface Bus, IEEE 488 interface)


54
62E1    r/w     GPIB (adapter 3)


82E0-82EF ----  GPIB (General Purpose Interface Bus, IEEE 488 interface)

82E1    r/w     GPIB (adapter 4)


82F8-82FF ----  serial port, description same as 03F8
83F8-83FF ----  serial port, description same as 03F8


A220      ????  soundblaster support in AMI Hi-Flex BIOS  ????


A2E0-A2EF ----  GPIB (General Purpose Interface Bus, IEEE 488 interface)

A2E1    r/w     GPIB (adapter 5)


AFFF    r/w     plane 0-3 system latch (video register)


B220-B227 ----  serial port, description same as 03F8
B228-B22F ----  serial port, description same as 03F8


C220-C227 ----  serial port, description same as 03F8
C228-C22F ----  serial port, description same as 03F8


D220-D227 ----  serial port, description same as 03F8
D228-D22F ----  serial port, description same as 03F8


C2E0-C2EF ----  GPIB (General Purpose Interface Bus, IEEE 488 interface)

C2E1    r/w     GPIB (adapter 6)


E2E0-E2EF ----  GPIB (General Purpose Interface Bus, IEEE 488 interface)

E2E1    r/w     GPIB (adapter 7)




                            MEMORY-MAPPED ADDRESSES


80C00000  Compaq Deskpro 386 system memory board register


55
80C00000 w      RAM relocation register
                bit 7-2    Reserved, always write 1's.
                bit 1 = 0  Write-protect 128-Kbyte RAM at FE0000.
                      = 1  Do not write-protect RAM at FE0000.
                bit 0 = 0  Relocate 128-Kbyte block at FE0000 to address 0E0000
                      = 1  128-Kbyte RAM is addressed only at FE0000.

80C00000 r      Diagnostics register
                bit 7   = 0  memory expansion board is installed
                bit 6   = 0  second 1 MB of system memory board is installed
                bit 5-4 = 00 base memory set to 640 KB
                        = 01 invalid
                        = 10 base memory set to 512 KB
                        = 11 base memory set to 256 KB
                bit 3   = 0  parity error in byte 3
                bit 2   = 0  parity error in byte 2
                bit 1   = 0  parity error in byte 1
                bit 0   = 0  parity error in byte 0 (in 32-bit double word)

56
                     Program Segment Prefix Data Structure


When DOS loads a program for execution it creates a data structure in memory 
called the "Program Segment Prefix", or PSP for short. This structure occupies 
the 256 bytes of memory immediately preceeding the memory occupied y the 
loaded program. The PSP contains useful information which is often accessed by 
the running program. The following table describes the structure of the PSP.



Offset   Description

 00      INT 20 instruction for CP/M CALL 0 program termination
 02      segment of first byte beyond memory allocated to program
 04      unused filler
 05      CP/M CALL 5 service request (FAR JMP to 000C0h)
         BUG: (DOS 2+) PSPs created by INT 21/AH=4B point at 000BE
 06      CP/M compatibility - size of first segment for .COM files
 08      remainder of FAR JMP at 05
 0A      stored INT 22 termination address
 0E      stored INT 23 control-Break handler address
 12      DOS 1.1+ stored INT 24 critical error handler address
 16      segment of parent PSP
 18      DOS 2+ Job File Table, one byte per file handle, FFh = closed
 2C      DOS 2+ segment of environment for process
 2E      DOS 2+ process's SS:SP on entry to last INT 21 call
 32      DOS 3+ number of entries in JFT (default 20)
 34      DOS 3+ pointer to JFT (default PSP:0018)
 38      DOS 3+ pointer to previous PSP (default FFFFFFFFh in 3.x)
         used by SHARE in DOS 3.3
 3C      apparently unused by DOS versions <= 6.00
 3D      (APPEND) TrueName flag 
 3E      (Novell NetWare) flag: next byte initialized if CEh
 3F      (Novell NetWare) Novell task number if previous byte is CEh
 40      DOS 5+ version to return on INT 21/AH=30
 42      (MSWindows3) selector of next PSP (PDB) in linked list
         Windows keeps a linked list of Windows programs only
 44      unused by DOS versions <= 6.00
 48      (MSWindows3) bit 0 set if non-Windows application (WINOLDAP)
 49      unused by DOS versions <= 6.00
 50      DOS 2+ service request (INT 21/RETF instructions)
 53      unused in DOS versions <= 6.00
 55      unused in DOS versions <= 6.00; can be used to make first FCB
         into an extended FCB
 5C      first default FCB, filled in from first command tail argument
         overwrites second FCB if opened
 6C      second default FCB, filled in from second command tail argument
         overwrites beginning of command tail if opened
 7C      unused
 80      Length of command tail
 81      Command tail terminated by 0D


57
                                    CREDITS



The following publications have proved useful in the production of SSD:


8086/8088 User's Manual, Intel 1989

PC Intern, Michael Tischer, Abacus 1992

DOS Programmer's Reference, Terry R Dettmann, Que 1988

Interrupt List edited by Ralf Brown. Including details of the multiplex 
interrupt, described by Robin Walker.


The author is grateful to the cooperation of the virus writer "Black Baron" 
in supplying copies of his polymorphic computer viruses and supplying 
information about the SMEG engine. As well as testing early versions of SSD 
against his own polymorphic viruses. Thanks Chris!


Program Design & Coding: Matthew Probert

Version 2.7 published by Servile Software, November 1994. All rights reserved.

58
With effect from version 2.4, SSD became SHAREWARE and you are required to 
register your copy or stop using it.

Registration costs 29.95 pounds sterling (UK pounds).

Please make cheques payable to "M. Probert" ONLY, and send with the enclosed 
order form (order.doc) to:

Matthew Probert
5 Longcroft Close
Basinsgtoke
Hampshire
RG21 1XG

Telephone 0256 478576



        ÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜ
        ÛÛßßßßßßßßßßßßßßßßßßßÝÛÛÛÛ             ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
        ÛÛ C>_               ÝÛßÛÛ             ³ COGNITIVE DEVELOPMENT BBS  ³
        ÛÛ                   ÝÛÛÛÛ             ³                            ³
        ÛÛ                   ÝÛÛÛÛ             ³ Providing a forum for A.I. ³
        ÛÛ                   ÝÛoÛÛ             ³ researchers and developers ³
        ÛÛ                   ÝÛoÛÛ             ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
        ÛÛÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÝÛ ÛÛ             ³ Basingstoke, Hampshire, UK ³
        ßßßßßßßßßßßßßßßßßßßßßßßßßß             ³                            ³
  ÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛßßßßßßßßßßßßßßÛ      ³ 0256 50086 24 hours a day  ³
  ÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛ ÍÍÍ/Í[ÄÄ]ÍÍÍ Û      ³                            ³
  ÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÄÄÄÄÄÄÄÄÄÄÄÄÄÄÛ      ³   300 baud to 14,400 baud  ³
  ÛÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÛÛÛÛ ÍÍÍ/Í[ÄÄ]ÍÍÍ Û      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
  ÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÜÜÜÜÜÜÜÜÜÜÜÜÜÜÛ
   ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß