Maidenhead Grid Square Locator
By Paul Maserang (N5PCA)

The Maidenhead Grid Square system is a method of stating any position on the
globe.  The full 6-character grid square takes the form of two letters, two
numbers, and two more letters (ie. EM02DK is the same as latitude 32ø25'N,
longitude 99ø41'W).  A grid square co-ordinate is obviously shorter and easier
to state than latitude and longitude.

A 6-character grid square co-ordinate is accurate to 1/12th of a degree (0ø05')
of longitude by 1/24th of a degree (0ø02'30") of latitude, which works out to
2.5 nautical miles north-to-south by 5.0 nautical miles east-to-west at the
equator.  A 4-character grid square is accurate to 1 degree of longitude by 2
degrees of latitude, and a 2-character grid square is accurate to 10 degrees of
longitude by 20 degrees of latitude.  The origin of the grid square co-ordinate
system is the south pole (latitude 90øS, longitude indeterminate).

This program is designed to convert latitude/longitude positions to Maidenhead
Grid Square co-ordinates, and vise versa.  Usage is fairly straight-forward,
but there are a few things to be aware of:

   (1) Latitude and longitude must be entered in degrees and minutes (DD.MM),
       not degrees and decimal fractions thereof.  For latitudes, DD can range
       from -90 to 90; for longitudes, DDD can range from -180 to 180; and in
       either case, MM can be 00 to 59.  The program checks for values outside
       the -90 to 90 and -180 to 180 ranges, but does NOT check for invalid
       MM entries (MM>59), so be careful with your latitude/longitude entries.
       MM values greater than 59 are reduced modulo 60, with the excess carried
       into the DDD portion (ie. an entry of 0.90 will become 1.30, which is
       equivalent to 1.5ø).

   (2) SOUTH latitudes and EAST longitudes must be entered as NEGATIVE numbers
       (ie. for latitude 32ø25'S, your entry should be -32.25).

   (3) Grid square entries may consist of the first two characters, first four
       characters, or all six characters; short entries will be optimized to
       the center of the square before computing the corresponding latitude and
       longitude.  Any grid square entry containing an odd number of characters
       or is longer than six characters is considered invalid.

   (4) In all cases, an invalid entry (other than MM described above) causes
       the program to return to the main menu.

   (5) When converting a grid square to latitude/longitude, keep in mind that
       the resulting latitude can be off by as much as 3 minutes of arc, and
       the longitude off by as much as 5 minutes of arc, due to the resolution
       limitations of the grid square system (described above).  However, this
       translates to a maximum error of only 5 nautical miles in any direction
       from the correct position, which is negligible for most purposes,
       including amateur radio work.