SBBSecho
				  Version 1.00
				Updated 06/17/95

	       FidoNet Packet Tosser for Synchronet BBS Version 2

			Copyright 1995 Digital Dynamics

                                  PO Box 501
                             Yorba Linda, CA 92686

		 Voice: 714-529-6328   BBS: 714-529-9525 V.32/V.32bis
		   FAX: 714-529-9721	    714-529-9547 V.FC
                  Fido: 1:103/705      ftp: netcom.com /pub/sb/sbbs

























Table of Contents
=================

Introduction.............................................................3
Terminology..............................................................4
Installation.............................................................6
AREAS.BBS Format.........................................................7
Configuration............................................................8
Running SBBSecho........................................................19
Command Line Switches...................................................20
Area Manager Remote Commands............................................21












































_______________________________________________________________________________
SBBSecho                              2                                Contents



Introduction
============

SBBSecho is a full-blown FTN echomail program (tosser/scanner) for Synchronet
BBS version 2. SBBSecho is level III implementation of the SMB v1.21
specification including support for HyperAllocated and LZH compressed message
bases.

It is intended to replace FTSC-1 (*.MSG) compatible echomail programs (GEcho,
Squish, FastEcho, Alexi/Mail, etc.) and SBBSFIDO with a single program
incorporating the standard features of echomail programs without the .MSG
phase (consuming disk space and time).

You will not need to use SBBSFIDO (*.MSG import/export utility for Synchronet)
or any echomail programs after you have installed SBBSecho.








































_______________________________________________________________________________
SBBSecho                              3                            Introduction



Terminology
============

FTN
~~~
FidoNet Technology Network: Any network using FidoNet standards for addressing,
mail packets, mail sessions, node lists, etc.

Zones, Nets, Nodes, and Points?
~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
FTN node addresses are like phone numbers, they are made up of multiple
components (four to be exact). The components are: zone, net, node, and point.
Each component is specified by a decimal (base-10) number, separated by symbols
(no spaces):

	Zone:Net/Node.Point

The zone represents the continent (if FidoNet) or the network number (if other
FTN network). All FidoNet nodes in North America have a zone 1 address. When
the zone is specified in an address, it is the first component and must be
followed by a colon. If the zone is not present in an address, the local
system's zone is assumed.

The net represents the network number of the FTN node. Duplicate net numbers
may exist between zones. If the net number is not present, the local system's
net is assumed.

The node number specifies an exact FTN node within a network. The node number
is the only required element of an FTN node address.

The point is an optional component which specifies a sub-node that does not
directly receive mail and is also not listed in the main FTN node list, but
instead gets all its mail from its boss-node (zone:net/node.0). When the point
is not specified, 0 (zero) is assumed (i.e. 1:2/3 and 1:2/3.0 are identical)
which indicates the system is not a point node address.

A 2D (2 dimensional) address refers to an FTN address containing just the
net and node numbers (i.e. 103/705).

A 3D (3 dimensional) address refers to an FTN address containing the zone,
net, and node numbers (i.e. 1:103/705), specifically excluding the point number
if it exists.

A 4D (4 dimensional) address refers to an FTN address containing the zone,
net, node, and optional point numbers (i.e. 1:103/705.1).

A 5D (5 dimensional) address refers to an FTN address consisting of a standard
3D or 4D address with an appended "@domain" (i.e. 1:103/705@fidonet.org).







_______________________________________________________________________________
SBBSecho                              4                             Terminology



Attach or FLO Mailer?
~~~~~~~~~~~~~~~~~~~~~
If you are using FrontDoor, InterMail, D'bridge, SEAdog, Dutchie, or any other
ArcMail *.MSG attach-style mailer, you are using what we will refer to as an
"Attach Mailer".

If you are using BinkleyTerm, Portal of Power, or any other FLO/CLO/HLO/DLO
style mailer, you are using what we will refer to as a "FLO Mailer".

Both types are supported equally by SBBSecho.

NetMail
~~~~~~~
Point-to-point (usually person-to-person) direct or routed messages.

EchoMail
~~~~~~~~
Group or conference messages of a particular subject matter. Usually
distributed on a regional or continental (e.g. FidoNet Zone 1 backbone) scale.
FTN style echomail areas have a unique area tag (name) associated them to
distinguish each area from the others.

Packet
~~~~~~
An FTN packet is a group of one or more messages contained in a single
uncompressed file. Packets may contain echomail and/or netmail messages.
Packets usually have a .PKT extension, although outbound NetMail packets for
FLO Mailers will have .?UT extensions (where ? is either O, C, D, or H). The
first eight characters of the filename may be anything, but are usually decimal
digits representing the date and time the packet was created. SBBSecho creates
temporary outbound packet files with a .PK_ extension and then renames them to
.PKT when they're completed. If you find any .PK_ files in your outbound
directory, don't worry. SBBSecho will find them the next time it is run and
continue packing them and sending them on their way.

Bundle
~~~~~~
An FTN bundle is a single file archive of one or more (usually compressed)
packets. Bundles will have file extensions where the first two characters
represent the day of the week the bundle was created (MO, TU, WE, TH, FR, SA,
and SU) and the third character of the extension is a number or letter. The
first eight characters of the filename may be anything, but are usually
hexadecimal digits representing the FTN node address (or relative address) of
the system that created the bundle. SBBSecho changes the file extension of bad
inbound bundles to .MO_, .MO-, or .MO.

Areafix/Area Manager
~~~~~~~~~~~~~~~~~~~~
Areafix is a synonym for area manager (the very first FTN area manager
program was called AreaFix). Area manager capabilities (remote adding/removing
of areas, changing compression type, etc) are built into SBBSecho, so therefore
no external area manager program is required. If you are not an FTN hub, then
the area manager portion of SBBSecho will probably not get any use on your
system.

_______________________________________________________________________________
SBBSecho                              5                             Terminology



Installation
============

To begin, copy the SBBSECHO.EXE, ECHOCFG.EXE, and AREAMGR.HLP files into your
Synchronet EXEC directory (usually C:\SBBS\EXEC), copy the SBBSECHO.CFG file
into your Synchronet CTRL directory (usually C:\SBBS\CTRL), and copy the
SBBSECHO.DOC file into your Synchronet DOCS directory (usually C:\SBBS\DOCS).

If you plan on using the 32bit DOS or OS/2 version of SBBSecho, you will need
to put the appropriate SBBSECHO.EXE file into your Synchronet EXEC directory
(unzip OS2.ZIP for the OS/2 version or DOS4G for the 32-bit DOS version).

Add the SBBSCTRL and SBBSNODE environment variables to your AUTOEXEC.BAT.
Example:

SET SBBSCTRL=C:\SBBS\CTRL
SET SBBSNODE=C:\SBBS\NODE1

Note: The node number used for the SBBSNODE environment variable is not
      important, use your NODE1 directory.

These environment variables must be present for SBBSECHO and ECHOCFG to
function correctly. Type "SET" at the DOS prompt to be sure they are listed
correctly.

You will also need to modify your existing MAILER.BAT (or FDRUN.BAT, IMRUN.BAT,
etc) file to accomodate the use of SBBSecho, or replace it with the MAILER.BAT
included with SBBSecho. If this is your first time setting up FidoNet, you will
not currently have a MAILER.BAT file set up, so use the one that is included
and modify it so that it reflects the proper drive letters and directories.

Next, SBBSecho expects to find the file AREAS.BBS in your Synchronet DATA
directory (usually C:\SBBS\DATA) unless you have overridden the default name
and/or location using the ECHOCFG program.  The format of this file is very
similar to the standard AREAS.BBS (which many echomail programs use, or can
at least export their native area file to this format - i.e. GEcho's GSETUP).

SCFG can also export your sub-boards to AREAS.BBS, but you're probably better
off modifying the AREAS.BBS file you're already using (if you are) or
converting your current echomail program's area file to AREAS.BBS. This is
because SCFG assumes the sub-board short name will be the same as the area's
tag (as shown in your echo list), but this may not always be the case - unless
you imported an AREAS.BBS or FIDONET.NA file into SCFG to begin with).












_______________________________________________________________________________
SBBSecho                              6                     Installing SBBSecho



AREAS.BBS Format
================

Lines beginning with a semicolon (;) are considered comments, and are ignored.

Each line is in the following format:

CODE	TAG	UPLINKS

Where:
	CODE is the internal code of the sub-board. Any unrecognized internal
		codes are considered "Passthru" (not imported to your BBS).

	TAG is the FidoNet tag as shown in your echo list (i.e. FIDONET.NA).
		If this is '*', then it will be considered a "badecho" area
		and will receive all messages for areas not otherwise specified
		in this file.

	UPLINKS is a list of FidoNet addresses which you wish to export mail
		to. At the very least, your hub's address should be listed
		here. Your address should NOT be listed here.

AREAS.BBS Example:

SBBS		SYNCHRONET	1:3615/50
SYNCDATA	SYNCDATA	1:3615/50
SYNC_SYS	SYNC_SYSOPS	1:3615/50

The amount of spacing between each element in the line is not important. Each
line can be up to 1000 characters in length.

So if your OLD AREAS.BBS file is in .MSG format (for example):

C:\FD\ECHO\SBBS 	SYNCHRONET	1:3615/50

It must be changed to match the example given above!



















_______________________________________________________________________________
SBBSecho                              7                        AREAS.BBS Format



Configuration
=============

In order to set up SBBSecho for your system you must run the included ECHOCFG
program. It should already be located in your EXEC directory. You may want to
put your EXEC directory in your DOS search path so you can execute SBBSECHO and
ECHOCFG from any drive and directory on your system.

Multiple configuration files can be used (but isn't usually required) for
multi-mailer systems. The default configuration filename is SBBSECHO.CFG
located in your Synchronet CTRL directory. You can override this by specifying
the name and location of the configuration file on the SBBSECHO and ECHOCFG
command lines. Example:

ECHOCFG D:\ECHO1.CFG
SBBSECHO D:\ECHO1.CFG

If you do not specify a configuration file, ECHOCFG and SBBSECHO will use
SBBSECHO.CFG located in your Synchronet CTRL directory.

Upon running ECHOCFG you will be brought to the main menu of the configuration
program. The path and filename of the configuration file being modified will
appear at the top of the menu. Following are screen captures of available menus
within the configuration program and an explanation of the options contained on
each of them.

	      É[þ][?]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
	      º 	   C:\SBBS\CTRL\SBBSECHO.CFG		 º
	      ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
	      º ³Mailer Type			FrontDoor/Attach º
	      º ³Maximum Packet Size		250K		 º
	      º ³Maximum Bundle Size		250K		 º
	      º ³Registration Number		UNREGISTERED	 º
	      º ³Nodes...					 º
	      º ³Paths...					 º
	      º ³Toggle Options...				 º
	      º ³Archive Programs...				 º
	      º ³Additional Echo Lists...			 º
	      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

Mailer Type:
	Selecting this option will toggle between the mailer types supported
	by SBBSecho, either FrontDoor (message attach) type mailers or Binkley
	(FLO file) type mailers.  Choose the one that matches your front-end
	mailer type.

Maximum Packet Size:
	This option allows you to set the maximum size of each outgoing
	echomail packet.

Maximum Bundle Size:
	Mail packets are normally packed into what are called "bundles" (unless
	a node is set up to receive uncompressed mail packets).  This option
	allows you to specify the maximum size of each outgoing mail bundle.

_______________________________________________________________________________
SBBSecho                              8                    Configuring SBBSecho



Registration Number:
	Upon registering SBBSecho with Digital Dynamics, you will be given a
	registration number.  You should select this option and enter the
	registration number you are given here.  If you have not yet registered
	the program, this should say "Unregistered".

Nodes...
	This option allows you to add, remove, and configure nodes that you
	will be sending mail to.  Selecting this option will bring you to
	a sub-menu which will look similar to the following:

				 É[þ][?]ÍÍÍÍÍÍ»
				 º    Nodes   º
				 ÌÍÍÍÍÍÍÍÍÍÍÍÍ¹
				 º ³ALL       º
				 º ³1:100/ALL º
				 º ³1:200/300 º
				 º ³2:ALL     º
				 º ³	      º
				 ÈÍÍÍÍÍÍÍÍÍÍÍÍ¼

	At the Nodes... sub-menu, pressing the INSert key will allow you to
	add a new node, pressing the DELete key will remove the currently
	highlighted node number, and pressing ENTER on the currently
	highlighted node will allow you to edit the options for that particular
	node from a menu like the following (note that the node number you are
	editing appears at the top of the window):

		    É[þ][?]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
		    º		    1:200/300		   º
		    ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
		    º ³Address		    1:200/300	   º
		    º ³Archive Type	    ZIP 	   º
		    º ³Packet Type	    2+		   º
		    º ³Packet Password			   º
		    º ³Areafix Password 		   º
		    º ³Areafix Flags			   º
		    º ³Status		    None	   º
		    º ³Direct		    No		   º
		    º ³Passive		    No		   º
		    ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

	Address:
		This is the address of the node you are editing, selecting it
		will allow you to change this to a different address. Using
		the "ALL" wildcard in place of one of the address components
		will allow you to configure settings for all nodes that meet
		that specication (e.g. all nodes in zone 1 can be specified
		as 1:ALL or all nodes in zone 1, net 103 can be specified
		as 1:103/ALL).





_______________________________________________________________________________
SBBSecho                              9                    Configuring SBBSecho



	Archive Type:
		This is the compression type to be used when packing mail
		bundles for this node.	Selecting this option will allow you
		to choose from a menu of currently configured archive types,
		like the following:

			       É[þ][?]ÍÍÍÍÍÍÍÍÍÍ»
			       º  Archive Type	º
			       ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
			       º ³ZIP		º
			       º ³ARC		º
			       º ³LZH		º
			       º ³ARJ		º
			       º ³PAK		º
			       º ³SQZ		º
			       º ³ZOO		º
			       º ³None		º
			       ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

		Selecting "None" will specify that this node is to receive
		uncompressed packets (no bundles).

	Packet Type:
		This is the packet type that will be used when creating mail
		packets for this node. The default packet type used by SBBSecho
		is 2+.	If you are a "point" address (e.g. 1:100/100.1) you
		should use either a type 2+ or 2.2 packet since type 2 packets
		do not support point numbers. Selecting this option will allow
		you to choose from a menu of currently supported packet types:

			       É[þ][?]ÍÍÍÍÍÍÍÍÍ»
			       º  Packet Type  º
			       ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
			       º ³2+	       º
			       º ³2.2	       º
			       º ³2	       º
			       ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

	Packet Password:
		This is a password that will be placed into each outgoing mail
		packet for this node.  Passwords are normally used for extra
		security when sending and receiving mail packets.  This node
		must also have the same packet password defined for your
		address and SBBSecho must be set up for secure operation (set
		in the 'Toggle Options' sub-menu) in order for this feature to
		function properly.









_______________________________________________________________________________
SBBSecho                             10                    Configuring SBBSecho



	Areafix Password:
		This is the password that will be required by this node (in
		the subject field) when it sends messages to the area manager
		(AreaFix).

	Areafix Flags:
		When additional echo lists have been defined (from the
		'Additional Echo Lists...' sub-menu) these flags determine
		which echo lists can be used by this node when processing area
		manager add requests.

	Status:
		This option determines the netmail status that will be set
		when SBBSecho sends out an areafix message or a file attach.
		Selecting this option toggles between None, Crash, and Hold
		status.

	Direct:
		When set to 'Yes' this option will add a Direct kludge line
		to messages that SBBSecho sends out (or create DLO/DUT files
		for FLO mailers).

	Passive:
		Setting this option to 'Yes' will prevent messages from being
		sent to this node without the need for altering the AREAS.BBS
		file.  This is useful for temporarily shutting off the messages
		to this node.  This option can be toggled on and off remotely
		via an area manager request.



























_______________________________________________________________________________
SBBSecho                             11                    Configuring SBBSecho



Paths...
	This option allows you to configure the paths and filenames which are
	used by SBBSecho.  Selecting this option will bring you to the
	following sub-menu:

	  É[þ][?]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
	  º		       Paths and Filenames		     º
	  ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
	  º ³Inbound Directory		    <Specified in SCFG>      º
	  º ³Secure Inbound (optional)	    None Specified	     º
	  º ³Outbound Directory 	    C:\IM\OUTBOUND\	     º
	  º ³Area File			    SCFG->DATA\AREAS.BBS     º
	  º ³Log File			    SCFG->DATA\SBBSECHO.LOG  º
	  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

	Inbound Directory:
		This is the directory where SBBSecho should look for inbound
		mail packets.  This is normally taken from whatever has been
		set in the SCFG program.

	Secure Inbound (optional):
		This is an optional directory where SBBSecho should look for
		secure inbound mail packets.

	Outbound Directory:
		This is the directory where SBBSecho will place outgoing mail
		packets and bundles.

	Area File:
		This is the path and filename of the file that SBBSecho will
		use as it's AREAS.BBS file.  By default SBBSecho looks for
		the file AREAS.BBS in the data directory defined in SCFG.

	Log File:
		This is the path and filename of the file that SBBSecho will
		use when logging events.  By default SBBSecho uses the file
		SBBSECHO.LOG in the data directory defined in SCFG.


















_______________________________________________________________________________
SBBSecho                             12                    Configuring SBBSecho



Toggle Options...
	These options allow you to toggle various features in SBBSecho.
	Selecting this option will bring you to the following sub-menu:

	   É[þ][?]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
	   º			 Toggle Options 		    º
	   ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
	   º ³Secure Operation					Yes º
	   º ³Swap for Executables				Yes º
	   º ³Fuzzy Zone Operation				No  º
	   º ³Fast Message Base Open				Yes º
	   º ³Store PATH Lines in Message Base			Yes º
	   º ³Store SEEN-BY Lines in Message Base		Yes º
	   º ³Store Unknown Kludge Lines in Message Base	Yes º
	   º ³Allow Nodes to Add Areas in the AREAS.BBS List	Yes º
	   ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

	Secure Operation:
		When set to 'Yes', SBBSecho will compare the origin of any
		incoming mail packets to the nodes in the AREAS.BBS file
		as messages are imported.  If a packet password has been
		defined for that node, it will also be compared to the
		password contained in the mail packet.	Packets and messages
		failing this security will not be imported.

	Swap for Executables:
		SBBSecho relies on external executable programs for extracting
		and compressing mail bundles.  This option tells SBBSecho to
		swap out of memory when running any of these executables,
		giving the executable programs more free memory to run in.
		This option is only used in the 16-bit DOS flavor of SBBSecho.

	Fuzzy Zone Operation:
		Some mail programs do not create netmail messages with zone
		information (INTL kludge line) or may only do so when sending
		between zones. This is a problem for systems that receive
		netmail for multiple addresses with different zones (AKAs with
		different zone numbers). Setting this option to "Yes" allows
		SBBSecho to guess what the correct originating and destination
		zone is based on the net and node portions of the destination
		address in netmail message.

	Store PATH Lines in Message Base:
		When set to 'Yes', SBBSecho will store the PATH lines from
		incoming echomail in the Synchronet message base headers (not
		the body text). This option is useful for troubleshooting
		routing/duplicate message problems.

	Store SEEN-BY Lines in Message Base:
		When set to 'Yes', SBBSecho will store the SEEN-BY lines from
		incoming echomail in the Synchronet message base headers (not
		the body text).  This option is useful for troubleshooting
		routing/duplicate message problems.


_______________________________________________________________________________
SBBSecho                             13                    Configuring SBBSecho



	Store Unknown Kludge Lines in Message Base:
		When set to 'Yes', SBBSecho will store any unknown kludge lines
		from incoming echomail in the Synchronet message base headers.
		This option is useful for troubleshooting problems.

	Allow Nodes to Add Areas in the AREAS.BBS List:
		When set to 'Yes', SBBSecho will allow nodes to add areas
		(via area manager) which are listed in the AREAS.BBS list.
		When set to 'No', SBBSecho will only allow nodes to add areas
		from any additionally configured echo lists which they have
		access to.












































_______________________________________________________________________________
SBBSecho                             14                    Configuring SBBSecho



Archive Programs...
	This option allows you to add or remove archive programs from SBBSecho.
	Selecting this option will bring you to the following menu:

			     É[þ][?]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
			     º	Archive Programs  º
			     ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
			     º ³ZIP		  º
			     º ³ARC		  º
			     º ³LZH		  º
			     º ³ARJ		  º
			     º ³PAK		  º
			     º ³SQZ		  º
			     º ³ZOO		  º
			     º ³		  º
			     ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

	At the Archive Programs... sub-menu, pressing the INSert key will allow
	you to add a new archive program. Pressing the DELete key will remove
	the currently highlighted archive program. And pressing ENTER on the
	currently highlighted archive program will allow you to edit the
	options for that particular prgram from a menu like the following (note
	that the name of the archive program you are editing appears at the top
	of the window):

	  É[þ][?]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
	  º			       ZIP			     º
	  ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
	  º ³Packer Name	  ZIP				     º
	  º ³Hexadecimal ID	  504B				     º
	  º ³Offset to Hex ID	  0				     º
	  º ³Pack Command Line	  PKZIP %f %s			     º
	  º ³Unpack Command Line  PKUNZIP %f %s 		     º
	  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

	Packer Name:
		This is the name that will be used to reference this particular
		archiving program.  This is also the name that should be used
		by nodes using areamanger to change their compression type
		remotely.

	Hexadecimal ID:
		This is a hexadecimal identifier that SBBSecho should look for
		when determining the compression type used on incoming bundles.
		In this example we are looking for the ID 'PK', '50' is the
		hexadecimal value for the letter 'P' and '4B' is the
		hexadecimal value for the letter 'K'.

	Offset to Hex ID:
		This is the byte offset (from the beginning of the file) where
		the hexadecimal ID for this archive program can be located.
		In this example we are looking at an offset of 0 bytes from the
		beginning of the file.


_______________________________________________________________________________
SBBSecho                             15                    Configuring SBBSecho



	Pack Command Line:
		This is the command line used by this archiving program for
		compressing files.  The '%f' command line specifier will expand
		to the name of the compressed file, the '%s' command line
		specifier will expand to the name of the file being compressed.

	Unpack Command Line:
		This is the command line used by the archiving program for
		UNcompressing files.  The '%f' command line specifier will
		expand to the name of the compressed file, the '%s' command
		line specifier will expand to the path where the file is
		being extracted to.











































_______________________________________________________________________________
SBBSecho                             16                    Configuring SBBSecho



Additional Echo Lists...
	This option allows you to add and remove additional echo lists which
	can be used by SBBSecho for area manager add requests.	Normally these
	will be used in addition to your AREAS.BBS file.  If you have the
	toggle option 'Allow Nodes to Add Areas in the AREAS.BBS List' set to
	'No', you MUST create at least one additional echo list if you wish
	to allow other nodes to add areas via area manager requests.

	Selecting this option will bring you to a sub-menu listing any
	additional echo lists you currently have defined:

			  É[þ][?]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
			  º  Additional Echo Lists  º
			  ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
			  º ³C:\BACKBONE\FIDONET.NA º
			  º ³			    º
			  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

	Pressing the INSert key will allow you to add a new echo list, pressing
	the DELete key will remove the currently highlighted echo list, and
	pressing ENTER on the currently highlighted echo list will allow you to
	edit information about that list:

	  É[þ][?]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
	  º			    Echo List			     º
	  ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
	  º ³Echo List Path/Name  C:\BACKBONE\FIDONET.NA	     º
	  º ³Forward Address	  None				     º
	  º ³Forward Password	  None				     º
	  º ³Echo List Flags	  BACK				     º
	  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

	Echo List Path/Name:
		This is the full path and filename of the echo list you are
		defining.  This list should contain the areatag names of areas,
		one per line, with any comments seperated from the areatag by
		at least one space.

	Forward Address:
		This is the address to forward area add requests to.  This is
		usually the node number of your hub, but is only necessary for
		echo lists containing areas that you do not already carry
		(have listed in your AREAS.BBS).

	Forward Password:
		This is the area manager password to use when forwarding
		requests.








_______________________________________________________________________________
SBBSecho                             17                    Configuring SBBSecho



	Echo List Flags:
		These are the flags required for a node to be able to gain
		access to this particular echo list.  These flags are defined
		for each node from the 'Nodes...' sub-menu.

		Selecting this option will bring you to a sub-menu where you
		may add and remove flags for this echo list.

			     É[þ][?]ÍÍÍÍÍÍÍÍÍÍÍÍÍ»
			     º	Echo List Flags  º
			     ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
			     º ³BACK		 º
			     º ³		 º
			     ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼









































_______________________________________________________________________________
SBBSecho                             18                    Configuring SBBSecho



Running SBBSecho
================

The command line for executing SBBSECHO is very similar to SBBSFIDO, although
some command line switches have been eliminated.

We suggest you use the following command lines:

For importing:

	C:\SBBS\EXEC\SBBSECHO /LES!

For exporting (Attach Mailer):

	C:\SBBS\EXEC\SBBSECHO /LIN

For exporting (FLO Mailer):

	C:\SBBS\EXEC\SBBSECHO /LINF

Remove all references to SBBSFIDO from your batch files (if you have any).
See the included MAILER.BAT as an example.

































_______________________________________________________________________________
SBBSecho                             19                        Running SBBSecho



Command Lines Switches
======================

usage: sbbsecho [cfg_file] [/switches] [sub_code]

where: cfg_file is the filename of config file (default is ctrl\sbbsecho.cfg)
       sub_code is the internal code for a sub-board (default is ALL subs)

SBBSecho will execute normally (for Attach Mailer operation) with NO command
line switches required. Command lines switches are used to cause SBBSecho to
_do_ or _not_ do specific operations. When used, command line switches
are prepended by a slash (/) character. Multiple switches can be specified
in one grouping (multiple /switch sets are supported, but not required).
Switch letters are not case sensitive. The available switch letters and their
descriptions are:

P: Do not import inbound packets or extract inbound bundles
X: Do not delete inbound packets (*.PKT) after they're imported
N: Do not import inbound netmail (packetized netmail and *.MSG)
D: Do not delete inbound netmail (*.MSG) after they're imported
I: Do not import inbound echomail
E: Do not export outbound echomail
M: Ignore echomail pointers (export all locally created echomail messages)
U: Update echomail pointers only (export no echomail messages)
T: Do not update echomail pointers (test export)
H: Export all echomail messages (including messages imported from FidoNet)
J: Ignore recieved bit on netmail (import even though flagged as received)
L: Create log file (data\sbbsecho.log)
R: Create report of import totals (text\sbbsecho.msg)
B: Import locally created netmail too (ignore the local flag)
A: Export ASCII characters only (override individual sub-board ex-ASCII strip)
F: Create packets for outbound netmail (necessary for FLO Mailer operation)
Y: Import netmail for unknown users to sysop (user #1)
O: Import all netmail regardless of destination address (unless flagged local)
S: Import private echomail override (strip private flag)
=: Change existing tear lines to === when exporting
!: Notify users via telegram of received echomail messages


















_______________________________________________________________________________
SBBSecho                             20                  Command Lines Switches



AREAFIX Commands
================

Remote area manager, or areafix, commands are used by uplinks to be able to
turn echo areas off and on, list currently connected areas, and more.

The following text is from the file AREAMGR.HLP which, after installation of
SBBSecho, should be located in your Synchronet EXEC directory.	It lists the
area manager commands available to the nodes which have been configured using
the ECHOCFG program:

All requests must be sent to 'SBBSecho' or 'AreaFix' (without quotes).
The message subject must contain the node's AreaFix password.

In the body of the message to Area Manager:

[+]<areaname>         Connect an area
-<areaname>           Disconnect an area
%HELP                 Request this message
%LIST                 Request a list of areas available to you
%QUERY                Request a list of areas to which you are connected
%UNLINKED             Request a list of areas to which you are not connected
%COMPRESSION <type>   Change the compression type (ARC/ARJ/LZH/PAK/SQZ/ZIP/ZOO)
%PASSWORD <password>  Change your AreaMgr password
%ACTIVE 	      Reconnect all temporarily disconnected areas
%PASSIVE	      Temporarily disconnect all connected areas
%+ALL		      Connect all available areas
%-ALL		      Disconnect all areas
[---]                 Everything below the tear line is ignored

NOTE: A compression type of NONE is also supported for uncompressed packets.
























_______________________________________________________________________________
SBBSecho                             21                        Areafix Commands