BOXMODEL DOCUMENTATION
                                  Version 4.0

             BOXMODEL is a program for investigating  the  performance
         of closed-box, vented-box  and  passive-radiator  loudspeaker
         systems as  determined  by  Thiele-Small  models.   It  is  a
         successor of the BOXRESPONSE program that is  easier  to  use
         and offers additional capabilities.

             This program is not intended to instruct  the  novice  in
         designing or building loudspeakers.  The user is expected  to
         have some familiarity with the Thiele-Small models and  their
         associated notation and terminology.   If  you  know  nothing
         about the models you should start by reading  about  them  in
         books such as  "Bullock  on  Boxes"  or  "Loudspeaker  Design
         Cookbook," both offered by Old Colony Sound Labs.


         1. MACHINE REQUIREMENTS

             BOXMODEL is designed for an IBM PC or compatible with  at
         least 460K of available RAM,  DOS  2.x  or  higher  and  with
         graphics capability.  The program will recognize and use CGA,
         EGA, VGA or MCGA video adapters.  I believe it should also  be
         usable with any adapter that is capable  of  emulating the high
         resolution modes of these adapters, but I have not been  able
         to verify this.  Color capability is not necessary, but it is
         highly recommended.

             Some of the data calculations in the program involve many
         floating  point  operations,  so  a  coprocessor  is   highly
         recommended.  If you run an 8088 machine with no coprocessor,
         you can expect waits of up to three minutes  while  the  data
         for four simultaneous graphs is computed.  With  an  8087  in
         place this wait drops to about 15 seconds.  To  achieve  this
         same time without a coprocessor, you need at least a  16  MHz
         386 machine.  The 8087 is available for about $120.


         2. PROGRAM OPERATION

             The program starts with a title screen.  Hitting any  key
         will take you to the main work screen.

             You operate the program by a menu and data entry  system.
         You can enter information  for up to four systems designated
         A, B, C, D.  The current active system, i.e., the one you are
         entering data for is  indicated in the lower right hand corner
         of the screen.  To switch to data entry for a different system,
         use the Files->Show selection to pick the system you want to make
         active.  Once chosen, you are entering data for only that
         system until you make another choice.  The performance of one
         or more of these  systems  is examined by using the  PLOT menu
         to  graph  various  system functions.


         3. DATA ENTRY

             The data entry system consists a  main  menu  from  which
         submenus or data windows are accessed.  The main menu is free
         form and consists of the items FILES, CONFIG, DATA, PLOT, MISC,
         ALIGN, and HELP which  are always displayed.  Main menu select-
         ions are made by pressing the RED capitalized letter of the
         desired item, or by moving the highlight onto the desired item
         with the LEFT and RIGHT ARROW keys and pressing the ENTER key.

         Procedure for Data Entry

             To enter data, first move the cursor to the data item you
         want to change by using the UP ARROW  and  DOWN  ARROW  keys.
         Then move into the data field with the RIGHT ARROW key.   The
         cursor will move the start of the data item.  Then  overwrite
         mode is active and you can simply write  in  what  you  want.
         The LEFT and RIGHT ARROW keys  let  you  move  to  any  field
         position.   The  SPACE  BAR  and  BACK SPACE   keys   delete
         characters.  Once  you  have  edited  to  your  satisfaction,
         striking the ENTER key will take you out of the field and you
         can move on to another field with the UP or DOWN  ARROW  keys
         or move back to the main menu by hitting the ENTER key again.

             If you are in a data field and have modified it, but then
         decide you want to keep the original value,  hit  ESC.   This
         will move you out of the  field  but  preserve  the  original
         value.  If you decide you really didn't mean to edit  any  of
         the fields in a window, hit ESC rather  than  ENTER  and  the
         cursor will move back to the main menu and all of the  fields
         in the window will be returned to  the  values  they  had  on
         entry.


         3. HELP

             Help can be summoned for most menu items by  highlighting
         the item and then pressing F1.  If there is anything  I  felt
         needed to be said about  the  item,  a  window  with  a  help
         message will pop up.  On a color system the  window  will  be
         green with black text.



         4.  MAIN MENU DETAILS

             The use of most main menu selections is  clear,  but  the
         following items merit additional discussion.

         DISPLAY
           The current system (A,B,C or D) is always displayed.
           Whether or not the current system is a maximally flat
           alignment or not is shown.  The Boxf3 item in the right 
           side middle of the screen is the box cutoff frequency 
           f3B. This cutoff applies only to the box acting alone, 
           whether or not there is an equalizer in the  system. 
           The complete system -3 dB frequency is listed under 
           Sysf3 and includes the effect of any equalizer.

           These cutoff frequencies are calculated by a numerical
           procedure that can go awry.  If this happens then usually
           the phrase 'Bad value' will appear rather than a number.
           Nevertheless, you should be suspicious of any extremely
           small number because it probably means an untrapped bad
           value. Usually this happens only when you have specified
           a  really wild set of parameters.  If you change to a more
           reasonable set, a reasonable number should reappear in
           this position.  The final item displays configuration of
           the current system.


    1. FILES

         1.1  Show
              The program  can  maintain  information  on  up  to  four
              different systems in memory, designated A, B,  C  and  D  for
              identification.  The particular system being displayed in the
              data entry window at any time is indicated in the upper
              center of the window frame.  To change to another, select 
              the Files->Show menu and pick the system who's information
              you want to show.  You will then be working with that system
              until you change it again using the Files->Show menu.

         1.2 dBase
             This selection will display a box with the current number of
             records available in the database.  You can load any of the
             drivers in the database by entering.  Those of you who have 
             a dBASE compatible database program, can look at the structure 
             and records.  Currently there are 1048 drivers in the FULL 
             version of this program's database.  There are drivers from 
             4.0" to 30.0". There are home hi-fi type drivers, PA type 
             drivers, and car stereo type drivers.  THE DEMO VERSION OF
             THIS PRODRAM CONTAINS ONLY 4 DRIVERS IN THE DATABASE.
             Make sure the file DEMO.DBF is in the same directory as 
             BOXDEMO.EXE otherwise you will get an error.

         1.3 Move
             This ÿallows ÿyou ÿto move the ÿsystem ÿcurrently ÿbeing
             displayed into any one of the four stored systems A, B, C or
             D.  ÿThus, for example,ÿyou can enter driver parameters into
             the ÿdisplayed system, ÿand quickly move them to any of ÿthe
             other systems.  This cuts down on data entry.

         1.4 GPrint
               
               THE DEMO VERSION OF BOXMODEL DOES NOT SUPPORT GRAPHICS 
               PRINTER DUMPS.

         1.5 Print
             This selection is provided for machines without a PRTSCR
             key.  It will send the system data currently on display
             to an attached printer if it is on line.  Otherwise, nothing
             will happen.  The window borders may look somewhat strange
             if your system doesn't support the IBM higher order chara-
             cter set or if you have not run GRAFTABL.COM in certain DOS
             versions, but all of the  data  should  be  sent  correctly.
             This  PRint SCReen function is not capable of dumping graphics
             screens to a printer.

         1.6 Exit
             Save current state and exit to DOS.


    2. CONFIG

         2.1 Speaker

             2.1.1 Driver
                   Single - Single driver in current system.
                   Series Isobaric - Dual drivers wired in series in an
                                     Isobaric Enclosure
                   Parallel Isobaric - Dual drivers wired in parallel in
                                       an Isobaric Enc.
                   Series Compound - Dual drivers wired in series in a
                                     Normal Enclosure
                   Parallel Compound - Dual drivers wired in parallel in a
                                       Normal Enclosure.

              2.1.2 Box
                    Closed - Select current system to be Closed Box Type
                    Vented - Select current system to be Vented Box Type
                    PR     - Select current system to be Passive Radiator
                             Box Type

              2.1.3 EqOrder
                    0  - No active equalization on current system.
                    1  - 1st order active equalization on current system.
                    2  - 2nd order active equalization on current system.
                    3  - 3rd order active equalization on current system.

         2.2 Program

              2.2.1 Graphs
                    A     - Plot just System A.
                    AB    - Plot System A and B.
                    ABC   - Plot System A, B and C.
                    ABCD  - Plot System A, B, C, and D.

                    Enter in any order.
              
              2.2.2 TempPr
                    The this selection is provided for those who prefer to
                    use their own values for ambient temperature and
                    barometric pressure.  The default values are in the
                    window when the program starts.

              2.2.3 Units
                    Toggle between U.S. customary units and MKS units.

              2.2.4 Load
                    Toggle between using the loudspeakers' voice coil
                    resistance or its' voice coil impedance.  i.e. When
                    looking at the maximum power graph, treat the amplif-
                    ier as a constant voltage source (Re) or as a constant
                    power source (Zvc).  Use of the Zvc toggle tends to
                    be a very conservative approach.

    3.  DATA

         3.1 Driver
             Thiele-Small parameters are entered by hand into the fields.

         3.2 Box
             Vb - Volume of Box for current system
             Fb - Vented Box Tuning frequency. (not displayed if Closed)
             Vd - Vent Diameter.  (not displayed if Closed system)
             Numb Vents - Current number of vents. (not displayed if Closed)
             Vp - Acoustic equivalent volume of passive radiator.( if passive 
                  radiator)
             Sp - Surface area of passive radiator.(if passive radiator 
                  system)

         3.3 Loss
             Qas - Absorption Losses of current system
             Qls - Leakage Losses of current system
             Qps - Port Losses of current system (not displayed if Closed)

         3.4 Eq
             The Eqdata item allows the entry  of parameters for a high-
             pass filter of the chosen order.  Thus, you can examine fifth, 
             sixth, seventh and eigth order equalized alignments, or simply 
             decide whether a rumble filter will help performance.

             Cr1 - Corner frequency of filter effect.
             dmp - Damping Coefficient (reciprocal of Q) for 2nd order 
                   section, dmp of 0.5 = +6.0 dB, dmp of 1.414 = -3.01 dB.
             Cr2 - Second corner frequency of filter effect. (Third order 
                   only)

         3.5 Power In
             Enter the Amplifier Power to be applied to each design in watts.
             Files->Show A,B,C or D then Data->Power In menu and enter the 
             applied wattage.

     4. PLOT
             Freq Response -Small signal response of all systems selected.
             Phase - Acoustic pahse response of all systems selected.
             Impedance -Input Impedance for all systems selected.
             Imp Phase -Phase of impedance for all systems selected.
             Group Delay -Group delay for all systems selected.
             Max Power -Maximum diplacement limited power for all selected systems.
             Max SPL -Maximum SPL for all systems selected. Based on Power-In.
             Driver Excur -Required excursion for applied wattage for each system.
             Vent Air Speed -If all systems are vented or if only one 
                             vented system is plotted.
             PR Excur -If all systems are passive radiators or if only one
                       passive radiator system is plotted.
             Step Response -Transient response of all selected systems.
             Separate Resp -If only one system is plotted, this displays the
                            contribution of the box, the equalization and
                            the overall systems response.

             Choosing Plots will cause a menu to drop down from which you
             select how many systems you want to display simultaneously.
             After this selection is  made there  will be a delay with the
             message "Calculating" displayed.  This is when the extensive
             floating point calculations are executed. Striking any key
             will then return you to the plot type menu where you can make
             another selection.  THE DEMO VERSION OF THIS PROGRAM DOES NOT
             SUPPORT GRAPHICS DUMPS TO THE PRINTER, but the full version
             provides that capability for over 300 printers.

             When a single system is plotted, extra information is shown
             in  some cases.  If the system is equalized, then three graphs
             are shown in the small-signal magnitude plot: the box alone,
             the equalizer alone and the combined response.


    5. MISC

         5.1 Driver Params
             Any system parameter that may be of interest is calculated
             by the program and displayed here.  The significance of most
             of them is self-evident, but a few need comment.

             In the list of DRIVER  parameters  QTS  is  the  parallel
             combination of  QES  and  QMS  and  Sns is the calculated
             sensitivity of the driver at 1 meter with input voltage
             equal to the square root of RE. This is the usual 1 watt/
             1  meter specification when the load impedance is R, and
             it  usually is fairly close to manufacturers spec sheet
             values.

         5.2 Coefficients
             Box Denominator Coefficients - Numerator coefficients of the
                 polynomial that describe the transfer function of the
                 box/driver combination of the current system.
             Box Numerator Coefficients - Denominator coefficients of the
                 polynomial that describe the transfer function of the
                 box/driver combination of the current system.
             Equalizer Denominator Coefficients - Denominator coefficients
                 of the polynomial that describe the transfer function of
                 the high-pass equalizer used in the current system.

         5.3 Box Dim - Size
             This menu option displays the internal box dimensions necess-
             ary for the current box volume.  The dimensions are given to 
             the closest 1/16".  Several standard ratios are provided.

         5.4 Fix Dim - Size
             This option is provided for circumstances that require at least
             one of the box dimensions to be fixed.  A typical case: An
             enclosure you are designing for your car subwoofer.  You can
             enter the distance you have available between the wheelwells
             and the package tray in the trunk of your car and the program
             would calculate the length the box has to be.

         5.5 Ratios - Size
             This option provides for the entry by the user of any dimens-
             ion ratio they would prefer, over those calculated in Box Dim 
             above.

         5.6 Show Alignment
             alpha - Compliance ratio Vas/Vb.
             h     - Tuning ratio Fb/Fs.
             delta - Compliance ratio Vap/Vas
             k1    - Cr1/Fs 1st order Equalization section.
             dmp   - Reciprocal of filter Q. ( 1.4142 = -3.01 dB at Corner)
                     Cut Filter -> 20.0 * Log10(1.0/1.4142) = -3.01 dB 
                     Boost Filter -> 20.0 * Log10(1.0/0.5)  = +6.02 dB
             k2    - Cr2/Fs 2nd order Equalization section.

         5.7 Vent Length
             The vent length for vented-boxes is calculated  from  the
             standard formula for one flanged and one unflanged end using
             the speed of sound as determined from the ambient atmospheric
             conditions given in the Temp & Pr window and the Vd (vent
             diameter) in the Data->Box menu.

    6. ALIGN
             Choose this option to create a flat alignment for the current
             selected system.

    7. HELP
             General comments and instructions on the operation of
             this software.